Back & Forth Professional API for upcoming release of v2.00

   Back & Forth Professional versions 1.25 and later are fully compatible
with the DOS 5 API task switcher standard as documented in the Microsoft
DOS 5 technical reference manual. Please consult it for further information/
examples.

   Back & Forth Professional also supplies a set of API calls for further
control of its environment. All Back & Forth Professional API calls 
originate through interrupt 12h. To initiate an API call, the registers 
should be filled as follows:

AX = 0fffeh
CX = 0fffeh
BX = function #

DX, ES, and DI may also be needed depending on function call.


                 Back & Forth Professional API Calls

Function #: 0  --  B&F Pro installed request.

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 0

Returned  : AX = 1 if B&F Pro installed

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 1  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 2  --  Get memory stats.

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 2

Returned  : AX = amount of available swap memory in kilobytes.
            BX = maximum task size in kilobytes.
            DX = fixed overhead per task.

** NOTE **  Fixed overhead does NOT include video saving/restoring, program
            code/data, or macro memory if macros are enabled in EMS memory.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 3  --  Switch task by ID value

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 3
            DX = Task ID value (see function 7 for makeup of ID)

Returned  : AX = 1 task switch will occur as soon as DOS is safe
            AX = 0 invalid task ID.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 4  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 5  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 6  --  B&F Pro version #

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 6

Returned  : AX = version #

            Major version # = AX / 100
            Minor version # = AX % 100

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 7  --  Spawn a program. BF_SPAWN record is passed in ES:DI

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 7
            ES = segment of BF_SPAWN record
            DI = offset  of BF_SPAWN record

Returned  : AX = 1 spawn will take place when it is safe
            AX = 0 no task handles available!

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 8  --  Get active task list. 

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 8
            ES = segment of task storage area
            DI = offset  of task storage area

Returned  : AX = # of tasks loaded

** NOTES ** The STORAGE AREA must be at least sizeof(BF_TASK) * 21 or you
            will have serious problems on your hand!

            See OEMTEST.C for a complete example of this function.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 9  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 10  --  Return active clipboard filename.

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 10

Returned  : DX:AX makes up a far ptr to a '\0' terminated filename.

** NOTE ** The cut/paste file is NOT in ASCII format... the next release
           of this document will have sample code to read/write B&F Pro
           clipboard files.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 11  --  Get active task #.

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 11

Returned  : AX = Active task # in range of 0 to 19. Information about the
                 task can be obtained by using this value as an offset into
                 the active task list (See function 8).
            BX = # of tasks allocated
            DX = Max # of tasks

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 12  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 13  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 14  --  Reserved.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 15  --  Put a '\0' terminated string of characters into the 
                    B&F Pro's internal keyboard buffer.

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 15
            ES = segment of string
            DI = offset of string

Returned  : Nothing.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 16  --  Is current video mode a text mode

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 16

Returned  : AX = -1 Graphics mode
            AX = 0  Color text mode
            AX = 4  Mono  text mode

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 17  --  B&F Pro user #

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 17

Returned  : AX = user # from 0 to 255

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 18  --  Switch task by task_no into active task list

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 18
            DX = Task # (see function 8 for obtaining active task list)

Returned  : AX =  1 task switch will occur as soon as DOS is safe
            AX =  0 an attempt was made to switch to the active task!
            AX = -1 the task # was invalid

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 19  --  Delete task.

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 18
            DX = Task # (see function 8 for obtaining active task list)

Returned  : AX =  1 task was deleted successfully.
            AX =  0 an attempt was made to delete the active task!
            AX = -1 the task # was invalid

** Note **  If you delete a task that was lower in the task list than the
            active task, the active task # will change! Use function call
            11 to regain active task #.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Function #: 20  --  Get next available task handle

Parameters: AX = 0ffffe
            CX = 0ffffe
            BX = 20

Returned  : AX =  1 to xx next available task handle
            AX = -1 task table is full.

** NOTE **  This function can be used to build a hot key, etc. If a task
            is NOT spawned immediately after this call, the task handle #
            returned may become invalid.


            Back & Forth Professional API Data Structures

1) BF_SPAWN record used in function 7.

   typedef struct
   {
     char description[21];         /* Task description                       */
     char disable_hot_keys;        /* On/off - some applications can't afford*/
     int  environment_size;        /* to be bothered.                        */
                                   /* Size of environment in bytes.          */
     char kb_flags;                /* Hotkey kbflags ALT,LSHIFT,RSHIFT,CTRL  */
     int  key_code;                /* Key code as retrieved at the int 9h    */
                                   /* level.                                 */
     int  max_ems_pages;           /* Not implemented in OEM versions of     */
                                   /* kernel.                                */
     int  memory_needed;           /* Needed memory in K.                    */
     char program_id[3];           /* Two letter Desqview style ID           */
     char program_name[13];        /* Name of program without path. EXE,COM, */
                                   /* or BAT extension must be supplied or   */
                                   /* program won't run!                     */
     char program_path[66];        /* Directory where program can be found.  */
     char work_path[66];           /* Initial path to start program in. If   */
                                   /* not specified, work path will be set   */
                                   /* to the program path.                   */
   } BF_SPAWN;


2) BF_TASK record used in function 8.

   typedef struct                  /* Record B&F passes back about live tasks*/
   {
     time_t actual_start_time;     /* Actual start time of program           */
     char   description[21];       /* Task description                       */
     time_t elapsed_time;          /* Actual time spent in task              */
     int    id;                    /* Task id                                */
     char   kb_flags;              /* Keyboard flags component of task hotkey*/
     int    key_code;              /* Keyboard code component of task hotkey */
     time_t stop_time;             /* Time task was suspended/exited         */
     int    task_handle_no;        /* B&F assigned task handle.. used to     */
                                   /* individual tasks!                      */
   } BF_TASK;