PMAP 2.10
                                   ---------

        PMAP (Program MAP) displays how your PC's memory is being used.
        It lists all active programs (including resident programs such
        as Sidekick and PCED), displays free memory areas and their
        locations, identifies device drivers, summarizes expanded (EMS)
        and extended (XMS) memory use, and details certain DOS data
        areas.

        Version 2.10 adds support for XMS (extended memory) and the HMA
        (high memory area).  We have found that the old switch syntax
        was becoming unworkable (PMAP was designed in the good old days
        when memory was memory), so we decided to bite the bullet and
        change the way some of the options work.  Some switches have
        been renamed to conform with current terminology (/X was for
        expanded memory, is now for XMS memory) and some usage has been
        changed.  For example, /S used to mean "display ONLY standard
        memory"; no, it means "display standard memory in addition to
        anything else that's selected."  We apologize to anyone who has
        to change batch files, etc., but we felt that the changes were
        necessary.

        | identifies information about new features for PMAP 2.0.

        Syntax summary
        --------------
        The command line syntax of PMAP is:

            pmap [program-list] [/options]

        The default behavior, if no arguments are supplied, is:

            PMAP /e /s /x       (or, yes, PMAP /sex)

        The program-list, if present, restricts the display of resident
        programs to those listed; the list may include wildcards (*).
        The program list affects the standard memory display only.  See
        "Standard memory display", below.

      | The option switches are:
      |
      |     Select primary displays(s):
      |         /e   display expanded (EMS) memory summary
      |         /k   display data area of DOS kernel (DOS 3.0 or later)
      |         /r   display raw list of memory blocks
      |         /s   display standard DOS memory
      |         /v   display device driver information
      |         /x   display extended (XMS) memory summary
      |
      |     Additional options for /s display (these all imply /s):
      |         /d   display detail list of allocation by programs
      |         /f   display names of open files (DOS 3.0 or later)
      |         /n   display programs' environments
      |
      |     Othe options:
      |         /q   quick display
      |         ?   display syntax summary

        Multiple switches may be specified together or separately.  All
        of these are valid and equivalent:

            pmap /f /d
            pmap /fd
            pmap /f/d

        If you wish to set "permanent" options, i.e., options that will
        be in effect for every PMAP run, set an environment variable
        called PMAP to contain the desired option switches.  For
        example, if you usually want to list only standard memory, with
        file handles, set PMAP as follows:

            SET PMAP=/s /f

        To override options set in the PMAP variable, you can follow
        any switch with an asterisk.  For example, if you have the PMAP
        variable set as above but do NOT want to see the file handles
        for one run, use:

            pmap /f*


      | Selecting the primary display(s)
      | --------------------------------
      | PMAP provides six primary displays:
      |
      |     - standard (conventional) DOS memory (/s option)
      |     - expanded (EMS) memory (/e)
      |     - extended (XMS) memory (/x)
      |     - the system kernel (/k)
      |     - device drivers (/v)
      |     - raw statndard memory blocks (/r)
      |
      | By default, PMAP displays the first three; as mentioned above,
      | you can change the default with the PMAP environment variable.
      |
      | The first occurrence of any of the above options, either on the
      | command line or in the PMAP variable, turns off all of the
      | others.  Thus, if you type
      |
      |     pmap /sk
      |
      | You will see only the standard memory and kernel displays--the
      | EMS and XMS displays are turned off.  Similarly, if you use
      |
      |     SET PMAP=/e
      |
      | you will, by default, see only the expanded (EMS) memory
      | display.
      |
      | Primary options set on the command line turn off any primary
      | options set in the PMAP variable:
      |
      |     SET PMAP=/s
      |     ...
      |     pmap /x
      |
      | In the example, only extended memory is displayed.
      |
      | Note that the /d, /f, and /n options all imply /s, since they
      | affect only the standard memory display.  Thus,
      |
      |     pmap /d
      |
      | is equivalent to
      |
      |     pmap /sd
      |
      | and will display only standard memory (including the details
      | requested by /d).


        Standard memory display
        -----------------------
        The display of standard (conventional) DOS memory looks similar
        to this:


          Addr Program   Parent    Parameters     Han Blks   Size    Vectors
          ---- -------  -------- ---------------  --- ----  -------  -------
          147D command  command  main               0    2     3888  2E
          157B nmi      command  /i/q               0    2     1856  02
          15F2 cache-em command  500                0    2    13168  13 19
          193E dbase    command  /C d:command      16    2   238384  30
          ...
          Other allocated blocks                         4    81296
          Total conventional free memory                 4   451696
          Largest conventional free block                    371168
          Next program will load at 5579

        Each program that is currently in memory is displayed.  Fields
        are as follows:

            Addr        The memory segment at which the program is
                        loaded, in hexadecimal.  If an asterisk (*)
                        follows the address, the program is loaded
                        into a disconnected high memory chain (see
                        below).

            Program     The name of the program, if available.  "n/a"
                        indicates that the name is not available.  The
                        program name is never available under DOS 2.x.

            Parent      The name of the program's "parent".  In most
                        cases, this will be "command", because most
                        programs are run by COMMAND.COM (i.e., from
                        the DOS prompt).  See below.

            Parameters  The command line parameters that were specified
                        when the program was run.  Some programs re-use
                        the area where the parameters are stored, in
                        which case a "??" will be displayed.  An
                        ellipsis ("...") at the end indicates that there
                        were more parameters than could fit here.

            Han         The number of open handles (or files) associated
                        with the owner.  See below.

            Blocks      The number of memory blocks that are owned by
                        the program.

            Size        The total size of all blocks owned by the
                        program.

            Vectors     A list of 80x8x interrupt vectors that appear to
                        have been "intercepted" by the program.

        In the example, the program NMI is loaded at memory segment
        157BH and was run directly from the DOS prompt or from a batch
        file.  The original parameters were "/i/q".  DOS has allocated
        two blocks of memory for the program, and they total 1856 bytes
        in size.  Vector 2 (nonmaskable interrupt) has been
        "intercepted" by NMI.

        "Other allocated blocks" refer to blocks of memory that are not
        free but also are not owned by any executable program that PMAP
        can identify.  They may be owned by device drivers or by DOS
        itself; or they may in fact be owned by executable programs but
        not indicated as such.  PMAP may be able to make an educated
        guess as to the true owner; if so, the probable name of the
        program will be indicated in parentheses when you use the /D
        option switch (see below).

        At the end of the list, PMAP indicates the number of blocks of
        free memory, the total size of all free blocks, the largest
        single free block, and the segment address at which the next
        program will probably load.

        You can restrict the display to certain programs by naming them
        on the command line.  For example, the command

            pmap sdump ced

        would display information for the SDUMP and CED programs, and no
        others.

        You can use a single wildcard '*' at the end of any named
        program in the list.  For example,

            pmap sd* c*

        would display information for all programs beginning with
        "sd" or "c".

        NOTE:  "below" the first program loaded in memory (usually
        COMMAND.COM), there is a block of memory allocated by DOS for
        device drivers, etc.  PMAP does not show this block in the
        main display; its size is indicated under "Other allocated
        blocks" area if you request a detailed listing (/D), and further
        detail is available with the /K switch (see below).


        Detail display (/D)
        -------------------
        When you run PMAP with the /D (Detail) option, you'll see the
        same display, except that PMAP will show a detailed list of
        memory blocks allocated for each program.  For example:

         Addr Program  Parent    Parameters  Han Blks  Size   Vectors
         ---- ------- -------- ------------- --- ---- ------- -------
         1666 kbfix2  command  /KT1 /D0...     0    2    2560 08 09 16
         1661  Environment                                 64
         1666  Program                                   2496

        KBFIX2 has two memory blocks allocated to it; PMAP shows the
        size of each block and its address, and makes an educated guess
        as to what the block is used for.

        You may include a list of specific programs to be displayed:

            pmap sdump ced /d

        PMAP also displays a detail list of all free blocks of memory
        and of "other allocated blocks".


        Environment display
        -------------------
        If you add a /N switch, PMAP will display the contents of each
        program's environment (if there is one).  For example, the
        command:

            pmap rxrun /n

        might display something like this:

         Addr Program  Parent    Parameters  Han Blks  Size   Vectors
         ---- ------- -------- ------------- --- ---- ------- -------
         B6D4  rxrun  command                  0    2    1536
         Environment [B7E3]
           COMSPEC=C:\COMMAND.COM
           PATH=C:\UTIL;C:\DOS
           PROMPT=$p$g
           [name] C:\BOOT\RXRUN.COM

        The [B7E3] represents the segment address at which the
        environment is located.

        The [name] field appears only under DOS 3.0 and later; it shows
        the contents of the area of the environment where the full path
        and name of the program are stored.  In some cases (especially
        in the case of COMMAND.COM), garbage may in fact be stored in
        this area.  If PMAP think that the field is invalid, it will
        report "[name field invalid]"; however, PMAP may display invalid
        data if the contents of the field look like displayable characters.


        Open files display (/F)
        -----------------------
        If the HAN field in the standard display is non-zero, the named
        program currently has files that are open.  You can display the
        names of these files by adding the /F option.  For example:

         Addr Program  Parent    Parameters  Han Blks  Size   Vectors
         ---- ------- -------- ------------- --- ---- ------- -------
         12CD  command  command  /f            1    2  4176  22 23 24 2E
         Open files: D:FOPT.TXT

        This feature is available only under DOS 3.0 and later and is
        mutually exclusive with the /Q (Quick) switch.


        Quick display (/Q)
        ------------------
        Some of what PMAP does can be somewhat time consuming on slower
        computer systems, and one task may fail under some versions of
        DOS.  If you would like PMAP to run slightly faster (about 1/2
        second on a 4.77Mhz machine if you have EMS) or if PMAP fails
        with an error message similar to:

                pmap: error tracing buffer chain

        then use the /Q (Quick) option switch.  With /Q set, PMAP will
        not:

            1. Search for a disconnected high memory chain, or
            2. Look for buffers, files, stacks, etc.

        The /K and /F options cannot be used with /Q.  Also note that /Q
        will have little effect on PMAP's speed unless you have expanded
        memory (EMS), and that /Q is automatically set for DOS versions
        prior to 3.0.

        Remember, if you always want to use the /Q switch, you can

            SET PMAP=/Q

        in your environment.


        Kernel display (/K)
        -------------------
        Below the first program loaded into memory (usually COMMAND.COM)
        there is an area of memory used by DOS for storage of code and
        data.  This area is broken into three major sections:

            1. IBMBIO's code and data.  This is always located at memory
            segment 0070h and contains the basic code and data for
            system input/output services.  The default device drivers
            (for the printer, screen, and keyboard, etc.) are also
            located here.

            2. IBMDOS's basic code and data.  This is located in memory
            immediately following IBMBIO's area and contains the "guts"
            of DOS.  This area usually includes space for five FILES
            and one BUFFER.  (Under DOS 5.0 with DOS=HIGH, part of this
            area is moved to the HMA.)

            3. A supplementary DOS data area.  This area may include:
                - your FCBs; the size is affected by the FCBS option
                  in your CONFIG.SYS.
                - any FILES beyond the initial number (usually 5) that
                  are stored in the IBMDOS area.  This size of this area
                  is determined by the FILES option in CONFIG.SYS.
                - any BUFFERS beyond the initial number (usually 1) that
                  are stored in the IBMDOS area.  The size of this area
                  is determined by the BUFFERS option in CONFIG.SYS.
                - your logical drive table.  There is one entry in this
                  table for each drive up to LASTDRIVE.
                - your DOS STACKS, if any (DOS 3.1 or later only).  The
                  size of this area is determined by the STACKS option
                  in CONFIG.SYS.
                - any externally loaded device drivers such as ANSI.SYS.

        To display a detailed map of the complete DOS memory area (all
        three of the above), use the /K option.  The display might look
        something like this:

           MCB Addr  End   Size  Contents
          ---- ---- ----  -----  --------
           --  0070 0279   8352  IBMBIO [includes 13 device drivers]
           --  027A 09C7  29920  IBMDOS [includes 5 files, 1 buffer]
          09C8 09C9 1282  35760  DOS data/drivers

          DOS data/drivers area detail:
               09C9 0E9B  19760    8 device drivers (PMAP /V for detail)
               0E9C 0F10   1872   35 files
               0F11 0F1E    224    4 FCBs
               0F1F 1191  10032   19 buffers
               1192 11B5    576    7 logical drives
               11B6 1282   3280    9 stacks (128 bytes each)

        The first section shows the locations and sizes of the three
        major areas used by DOS.  In this case, for example, area 2 (the
        basic IBMDOS code/data area) begins at memory segment 027Ah and
        is 29,920 bytes in size.  It includes five files and one buffer.

        The MCB field, which only appears for area 3, shows the address
        of the memory control block for the area.  This is part of DOS's
        memory management scheme and is decribed in greater detail later
        in this manual.  Areas 1 and 2 are not part of DOS's official
        memory chain, so they have no MCBs.

        The second section breaks down the contents of area 3 in greater
        detail.  In the example system, eight device drivers are
        loaded and the system is configured as follows:

                FILES=40
                BUFFERS=20
                LASTDRIVE=G
                STACKS=9,128
                FCBS=4,0

        The display shows the exact location and size of each of these
        items.  For example, the extra 19 buffers (there's one in area
        2, leaving 19 of the 20 for area 3) are located at memory
        segment 0F1Fh and extend through the end of memory segment
        1191h, a total of 10,032 bytes.

        If you use an extender program such as QEMM's FILES.COM to
        increase the number of FILES after bootup, storage for the extra
        files will be located elsewhere in the memory chain--not in
        any of the DOS data areas described.  PMAP will display such
        areas in a separate section if there are any.  For example, if
        we ran:

            FILES + 2

        to increase the maximum number of files from 40 to 42, the
        display might appear as follows:

            Additional memory block(s) used for DOS data:
             MCB Addr  End   Size  Contents
            ---- ---- ----  -----  --------
            1897 1898 18C8    784
              >> 18C1 18C7    112   2 files

        This shows that the 944-byte block from 1403h to 143Dh (with MCB
        at 1402h) is used for supplementary DOS data.  Within this
        944-byte allocation, the 272 bytes from memory segments 142Ch
        through 143Ch contain the actual storage for information about
        the five files.

        Note also that, if there are additional blocks such as these,
        they are identified in the standard program display if you use
        the /D (detail) option.  The above might look something like
        this in the detail display:

         Addr Program  Parent    Parameters  Han Blks  Size   Vectors
         ---- ------- -------- ------------- --- ---- ------- -------
         1898 n/a     command  +2              0    1     784
         1898   2 files                                   784

        The /K option is available only under DOS 3.0 and later.


        Raw display (/R)
        ----------------
        When you run PMAP with the /R (Raw) parameter, you'll see a
        display like this:

            T  MCB  Addr  Owner  Para    Bytes
            - ----  ----  -----  ----  --------
            M 0974  0975   0008  0AFA     44960
            M 146F  1470   1470  00C3      3120
            M 1533  1534   1470  0020       512 GLVMGR
               [more of the same]
            M 1DF3  1DF4   1DF4  0706     28768
            M 24FA  24FB   2500  0004        64 [pmap]
            M 24FF  2500   2500  1376     79712 [pmap]
            Z 3876  3877   0000  6789    424080

        This is an uninterpreted list of all blocks of memory allocated
        by DOS (see below).  The fields are as follows:

            Type        The block type.  There are only two block types,
                        type M and type Z.  The last block in the
                        chain is type Z, and all others are type M.

            MCB         The segment address of the Memory Control Block
                        (sometimes known as an arena header).

            Addr        The segment address of the memory block itself.
                        This is always equal to the MCB address plus
                        one.

            Owner       The segment address of the program that "owns"
                        the block of memory.  If this is 0000, the block
                        is unallocated or "free".

            Para        The size of the block, in paragraphs (16 bytes).

            Bytes       The size of the block, in bytes.

        All numbers are hexadecimal except "bytes", which is decimal.

        The [pmap] suffix after an allocated block indicates that the
        block is being used by PMAP.  When PMAP terminates, this block
        will be free (unallocated).  The standard (non-raw) PMAP display
        understands this, and displays the map as if PMAP weren't there.

        Following some lines on the display you may see a one- to
        eight-character string:

            T  MCB  Addr  Owner  Para    Bytes
            - ----  ----  -----  ----  --------
            M 1533  1534   1470  0020       512 GLVMGR

        Under DOS 4.0 and later, a program name may appear in the last
        eight bytes of a memory control block (which is what the raw
        display is showing).  Under DOS versions prior to 4.0, DOS does
        not place the program name in this location, but some other
        programs (such as 386MAX and QEMM) may do so.  If PMAP thinks
        that the contents of the last eight bytes of the MCB look like a
        readable string, it will display the string.  This may provide
        some information about the owner of the block.  In some cases,
        the information in this area may be garbage that happens to
        consist of all ASCII characters--and these will be displayed.
        You should be able to tell at a glance which strings are
        meaningful and which are not.

        If PMAP is able to identify a disconnected high memory chain, it
        will display the line:

            Disconnected high memory chain:

        between the regular low-RAM DOS memory chain and the "hidden"
        high memory chain.

        If the /R switch is included, all other command line parameters
        are ignored.


        Expanded memory display (/E)
        ----------------------------
        If expanded (LIM or EEMS) memory is present and you have not
        specified /E*, PMAP displays EMS allocation as follows:

            Expanded memory summary:

                    Block      Size    Name
                    -----    -------   ----
                    0         589824   SYSTEM
                    1         425984
                    2          16384   CDIR
                    3          65536   HINDSITE
                    ...
                    Free      327680
                    Total    2097152
                    Page frame segment: CC00h

        The NAME field will be present only if your expanded memory
        manager supports the LIM 4.0 specification, and then only for
        programs that have defined their names to the system.

        EMS memory uses a "page frame" that maps a 64K block (actually,
        four 16K "pages") of EMS memory into standard 80x8x memory.
        The segment to which this memory is mapped is also displayed.


      | Extended memory display (/X)
      | ----------------------------
      | If extended memory (XM) is present and you have not specified
      | the /X* option, PMAP displays XM information as follows:
      |
      |     Extended memory summary:
      |
      |       INT 15 ext mem available               0
      |       XMS version                         3.00 (vendor 5.12)
      |       HMA                              enabled, in use
      |       Free XMS                          458752
      |       Largest free block                458752
      |
      |       XMS handles in use:
      |           Handle      Size  Address   LkCt
      |           1          32768  00110000    1
      |           2         277504  00118000   --
      |
      | "INT 15 ext mem" refers to AT-style extended memory that is not
      | managed by an XMS driver.  This type of memory is used primarily
      | by older devices such as VDISK.
      |
      | The remaining information is shown only if an XMS (eXtended
      | Memory Specification) driver is present in the system.  XMS
      | drivers manage extended memory by allocating and providing
      | access to blocks of XM as requested by system and application
      | programs.  Among such drivers are DOS's HIMEM.SYS, Qualitas's
      | 386MAX, and Quarterdeck's QEMM.
      |
      | "XMS version" is the version number of XM Specification that is
      | supported by your XMS driver.  Following this is the vendor's
      | internal version number for the driver software.
      |
      | "HMA" refers to the High Memory Area, a block of memory
      | approximately 64K in size at the very top of your CPU's real
      | mode address space.  The HMA is special because it includes the
      | only addresses above 1MB that can be accessed by the CPU in real
      | mode (which is the mode DOS normally uses).  Current XMS
      | managers allocate this space to one, and only one, program at a
      | time.  HMA is the are of memory that is used by DOS 5.0 when
      | DOS=HIGH is specified (thus moving most of DOS out of the lower
      | 640K).  PMAP's report shows whether or not the HMA is enabled
      | and, if so, whether or not it is in use.
      |
      | "Free XMS" shows the total amount of XMS-managed extended memory
      | that is current available for allocation, in bytes.  "Largest
      | free block" shows the size of the largest single free block of
      | XMS-managed memory.
      |
      | If any XMS-managed memory is currently allocated, the "XMS
      | handles in use" section displays additional information.  For
      | each active XMS "handle" (each block of extended memory
      | allocated by the XMS manager is assigned a handle), PMAP
      | displays the handle number, the size of the block in bytes, and
      | the 32-bit linear address of the block (in hex).  If the block
      | is currently "locked" (guaranteed not to move), PMAP displays
      | its non-zero "lock count", which is the number of times it must
      | be unlocked before it is once again movable.  Most blocks should
      | be unlocked most of the time.


        Device driver display (/V)
        --------------------------
        If you execute PMAP with the /V switch, it will display a table
        of information about your installed device drivers.  No other
        data (i.e., no memory maps) are displayed when /V is selected.

        The first five columns of the table contain the following
        fields:

            Name        If the device is a character device, the device
                        name.  If it is a block device (like a disk),
                        this will be "Blk (n)", where n is the number
                        of units handled by this device.

            Address     The address where the device driver begins in
                        memory, in standard hex segment:offset form.

            Size        The approximate size (in bytes, displayed in
                        decimal) of the device driver.  See below.

            Strt        The entry point of the driver's strategy
                        routine.  This is the hex offset within the
                        device driver's segment (shown under ADDRESS).

            Intr        The entry point of the driver's interrupt
                        routine.  This is the hex offset within the
                        device driver's segment (shown under ADDRESS).

        The remaining columns are bit fields with the driver's attribute
        record.  In each case, an asterisk indicates that the bit is
        set (1), and a space indicates that it is reset (0).

            CHR         *    = this is a character device
                        <sp> = this is a block device.

            IOC         *    = device supports IOCTL calls

            IBM    for block devices:
                        *    = non-IBM format
                   for character devices:
                        *    = supports output-until-busy

            RMV         *    = supports removable media

            LOG         *    = supports Get/Set Logical Device

            CLK         *    = this is the clock device

            NUL         *    = this is the NUL device

            SOT         *    = this is this standard output device

            SIN    for block devices:
                        *    = supports generic IOCTL
                   for character devices
                        *    = this is the standard input device

        Note that <space> implies the opposite of <*>; for example, an
        asterisk in IOC indicates that the device supports IOCTL calls,
        while a space there indicates that IOCTL is not supported.

        Also note that DOS does not provide any documented way for
        programs to find the chain of device drivers.  If PMAP is unable
        to find the chain, it will tell you so.


        Device driver size; order of list
        ---------------------------------
        PMAP cannot reliably determine the size of the default devices
        (CON, PRN, AUX, COM1, etc.) that are loaded automatically by DOS
        (they share code and data).  These will all show an address
        beginning with "0070", and their sizes will not be displayed.
        However, if you load a replacement for one of these devices (for
        example, ANSI.SYS loads a replacement for CON), PMAP will
        generally be able to determine and display its size.

        The devices are shown in the order in which DOS searches for
        them.  If there are two or more devices with the same name, the
        one that DOS will use is the first one listed.  For example, you
        will have two or more CON devices if you use ANSI.SYS; the
        ANSI.SYS CON will be listed before the default CON.  DOS will
        use the first one listed (ANSI.SYS).


        Disconnected high memory chains
        -------------------------------
        DOS manages memory by using a "chain" of allocated memory blocks
        as described below.  This chain normally ends at the 640K mark
        (segment A000), as memory addresses above this address are
        reserved for use by video adapters (some programs such as
        EEMRAM, QEMM, and 386MAX may extend the chain to B000 or B800).
        By following the links in this chain, PMAP is able to map your
        DOS memory and determine what programs own what areas of memory.

        However, Quarterdeck's QEMM and Qualitas' 386MAX may create an
        additional chain of allocated memory blocks in "high RAM" above
        the video adapter memory area.  Using a "high load" feature,
        these programs can load your resident utilities and device
        drivers into the high RAM chain, thus increasing the memory
        available to DOS in low RAM.

        The high RAM chain is not connected to DOS's standard low RAM
        chain (unless you use 386MAX's OPENHIGH option), and versions of
        PMAP prior to 2.0 would not find it; therefore programs loaded
        into high RAM were not displayed.

        Beginning with version 2.0, however, PMAP attempts to locate
        these "high memory chains" and identify the programs loaded
        there.  If PMAP succeeds in finding the chain and there are
        programs loaded in it, such programs will be marked with an
        asterisk (*) in the program display.  In raw block display mode
        (/R), the two chains (low and high) are shown separately.

        NOTE:  PMAP has no internal knowledge of QEMM, 386MAX, or
        similar programs; the presence of high memory chains is
        determined empirically.  The possibility exists that PMAP may
        occasionally report an artifact chain: something that looks to
        PMAP like a high memory chain but really isn't.  You should be
        able to tell by looking at the displays (especially the /R raw
        display) if such a chain has been found.


        Interrupt vectors
        -----------------
        Many times interrupts are "intercepted" by more than one
        resident program.  PMAP will only show a vector attached to the
        LAST program that intercepted it.  For example, in the sample
        display shown for the /D (Detail option), KBFIX2 shows that it
        has intercepted vectors 8, 9, and 16.  However, RXINTMGR and
        SDUMP could also have intercepted any or all of these three
        vectors, and PMAP would not know about that.

        PMAP assumes that any vector that points into memory owned by a
        program has been intercepted by that program.  That is not
        always true, so you may occasionally see spurious vectors
        attached to a program.


        More about parents
        ------------------
        Every program has a "parent"; if program B was executed by
        program A, then A is B's parent.  In most cases, the parent will
        be COMMAND.COM, because most PC programs are executed by
        COMMAND.COM.

        However, any program can execute any other program (assuming
        that there is sufficient memory, etc.).  This is how "shells"
        work.  For example, current versions of WordPerfect and many
        other programs allow you to "exit to DOS"; what they usually do
        is execute COMMAND.COM, which then displays a DOS prompt and
        allows you to enter any commands that you wish.  If you run
        PMAP, you will see two copies of COMMAND.COM in memory.

        However, you may notice that the second copy of COMMAND.COM
        shows COMMAND.COM as its parent.  Logically, you would expect
        the parent to be (in this case) WordPerfect.  Unfortunately,
        some versions of COMMAND.COM (the one that comes with DOS 3.2,
        for example) fool around with the area of memory that PMAP uses
        to find the parent's address; rather than having the parent's
        address, COMMAND.COM puts its own address there.  In effect,
        COMMAND.COM is always its own parent.

        In general, programs that allow you to execute other programs
        can use one of two methods:  they can execute the other programs
        directly, or they can execute COMMAND.COM and ask it to run the
        requested program.  If the former case, PMAP will show the true
        parent; if the latter, PMAP may show COMMAND.COM as the parent,
        and COMMAND.COM will be its own parent.

        Here is part of a PMAP display that shows a direct-execution
        under DOS 3.2:

            Addr  Program    Parent   Han  Blks    Size    Vectors
            ----  -------   --------  ---  ----   -------  -------
            ...
            3222  xced      command     0     2     26016
            387E  qe        xced        0     3     97232
            503E  command   command     0     3      3488  22 23 24
            ...

        The XCED program was run by COMMAND.COM (from the DOS prompt).
        It then ran the program QE directly, i.e., without reloading
        COMMAND.COM; QE's parent is correctly shown as XCED.  Finally,
        a "shell" exit was taken from QE, which did reload COMMAND.COM;
        notice that COMMAND shows as its own parent.  The second
        COMMAND.COM's real parent is QE, but this is not shown
        correctly.


        File handles
        ------------
        The "Han" field of the standard memory display shows the number
        of file handles that are associated with each program.  For the
        most part, this field will be zero.  Some open handles may show
        for programs that are active (for example, the active program
        named "dbase" in the first example has 16 open files).

        Use the /F option to see the names of the open files.

        You may see some resident programs that show one or more open
        handles.  This usually occurs when you redirect the program's
        start-up logo to NUL, and the program fails to close its
        standard files before exiting back to DOS (this really shouldn't
        be necessary, but it is).  These open handles may reduce the
        number of files your application programs can have
        simultaneously open.  We prefer not to redirect programs' logos
        to NUL.  We save file handles; we get to see the names of the
        nice people who wrote our software, and their copyrights; and we
        don't lose the error messages that explain why the program isn't
        doing what we thought it should.  Sounds like a bargain.


        Multi-tasking/task-switching programs
        -------------------------------------
        ... play havoc with the memory allocation chain.  PMAP may
        not yield very much useful information under such programs.


        DOS's memory allocation chain
        -----------------------------
        This information is almost totally undocumented by Microsoft, so
        take it for what's it's worth.  It's provided for informational
        purposes only, and could vary from DOS version to DOS version.
        However, the basic structure of the memory allocation scheme has
        remained unchanged from DOS 2.0 through the version that is
        current as of this date (5.0).  Only the program name field has
        changed--it was added with version 4.0.

        DOS (version 2.0 or later) manages memory as a chain of "blocks"
        or "arenas".  Each block begins on a paragraph boundary, can be
        (in theory) almost a megabyte in size, and is preceded
        immediately by a 16-byte Memory Control Block (MCB), sometimes
        known as an "arena header".  The lowest (the 80x8x interrupt
        vectors, BIOS and DOS data areas, DOS itself, device drivers,
        etc.) and highest (video buffers, ROM modules) portions of
        memory are not mapped, but the rest of memory is.  Thus, memory
        can be pictured like this:

            paragraph   contents
            ---------
              0000      low memory (unmapped)
                        first MCB (16 bytes)
                        first memory block
                        next MCB
                        next memory block
                        ...
                        last MCB
                        last memory allocation block
              nnnn      end of DOS memory (640K, for example)

        The address of the first MCB will vary, depending on your
        version of DOS and the number and size of device drivers,
        buffers, stacks, etc., that you loaded via CONFIG.SYS.  In all
        current versions of DOS (verified through 5.00), the segment
        address of the first MCB can be obtained via DOS function 52H.
        On return from this function, the address of the first MCB is
        located at ES:[BX-2].  Here is sample code that returns the
        address of the first MCB in AX:

            mov ah,52H
            int 21H
            mov ax,es:[bx-2]

        The MCB itself is a 16-byte region of memory that with fields as
        follows:

            Offset  Size    Contents
            ------  ----    --------
            0       Byte    'M': this is not the last MCB
                            'Z': this is the last MCB
                            anything else: memory control blocks
                            destroyed.  DOS will politely crash.

            1       Word    The segment address of the program that owns
                            this block of memory (the program's PSP).

            3       Word    The size of the block, in paragraphs

            5-7             Reserved

            8-15     n/a    8-char (blank-filled) name of owner program
                            (DOS 4.0+ only)

        This structure provides all of the information needed to step
        through the memory allocation chain.  A basic algorithm is as
        follows:

            Set MCB = segment of first MCB (as described above)
            Do Until byte (MCB:0) = 'Z'
                If byte (MCB:0) isn't 'M' or 'Z',
                    Then there's a big problem (the system is about
                    to crash with a "memory allocation error")
                Block_owner = word (MCB:1)
                Block_size = word (MCB:3)
                MCB = MCB + block_size + 1
            End

        EMS and XMS memory is not mapped by DOS.

        For more complete detail about DOS's memory allocation, see
        "Managing Memory" by William J. Redmond in PC Tech Journal,
        August, 1984 (Vol. 2, No. 2).

        Version 2.10 (7/3/91)
        ---------------------
        - Adds support for XMS drivers.
        - Reworks option switches.
        - Supports DOS 2.x and 3.x programs that deallocate their
          environment and place a smaller environment (containing
          just the program name) in their own primary allocation block.
        - Displays all selected primaries; previous versions would
          display (e.g.) only the kernel if /k was selected.
        - Fixes a problem that caused some deivces to show negative
          sizes.

        Version 2.03
        ------------
        Fixes a problem in displaying disconnected high-memory chains
        and resident programs loaded there.

        Version 2.02
        ------------
        - Fixes a problem with the "largest conventional free block".
        - Fixes problems with sizes of certain device drivers.
        - Fixes problem with stack size display when "STACKS=0,0".
        - Doesn't show the DOS data area as "unallocated".
        - Increases the maximum allowable number of files, buffers, and
          FCBs to 255 each (from 100).
        - Reduces chance of displaying spurious high memory chains.
        - Displays name field of environment (/E switch) only if all
          characters in the field are in the displayable ASCII range
          (33..127).
        - Displays name field in raw display only if the field contains
          an 8-character, blank-filled, displayable ASCII string, and
          only if the block owns itself (implying that it's a program).
        - Shows segment address of environment (/E switch).

        Version 2.01 (6/7/90)
        ---------------------
        Fixes a problem that prevented PMAP from working on systems
        with no expanded memory.

        Version 2.00 (6/5/90)
        -----------------------
        - Attempts to identify disconnected high-RAM chains
        - Adds /F (files) option
        - Adds /E (environment) option
        - Adds /K (kernel display) option and identifies areas of the
          DOS data block used for files, buffers, stacks, etc.
        - Adds /Q (quick display) option
        - Supports permanent options via PMAP variable
        - Correctly reports size of last installed device driver
        - Supports altered switch characters
        - Shows program name in raw display if available from
          environment.
        - Uses correct number of available file handles with extended
          handle tables (old versions assumed 20 handles)

        Version 1.34 (11/15/88)
        -----------------------
        Fixes a bug in 1.33 for resident programs that release their
        environments under DOS 4.0.

        Version 1.33 (11/14/88)
        -----------------------
        Uses a new feature of DOS 4.0 to more reliably obtain names of
        resident programs, including those installed via INSTALL.

        Version 1.31/1.32 (7/29/88)
        ---------------------------
        Displays number of open handles for each PSP.
        Displays sizes of some devices (/V switch).
        Improved display when too many vectors to fit on one line.
        Fixed spurious errorlevel returned by successful run (32).

        Version 1.30
        ------------
        Adds /X, /S, and /? switches.
        Adds device driver display (/V).
        Displays names of EMS-users when available (LIM 4.0 only).
        Allows wildcards in program-list.
        Fixes problem with name of secondary copies of COMMAND.COM
            under DOS 3.3 (it's not available).

        Version 1.26
        ------------
        Corrects a problem detecting extended memory with certain
        versions of BIOS ROM.

        Version 1.25
        ------------
        Adds the extended memory display and the selective display
        option.

        Corrects a minor problem with DOS 3.3.

        Version 1.21
        ------------
        Bug fixes to version 1.20:

        1. No more runaway display when EMS memory is present but none
        of it is in use.

        2. PMAP is more careful about what it thinks is the name of the
        command shell.


        Copyright/License/Warranty
        --------------------------
        This document and the program file PMAP.EXE ("the software") are
        copyrighted by the author.  The copyright owner hereby licenses
        you to: use the software; make as many copies of the program and
        documentation as you wish; give such copies to anyone; and
        distribute the software and documentation via electronic means.
        There is no charge for any of the above.

        However, you are specifically prohibited from charging, or
        requesting donations, for any such copies, however made; and
        from distributing the software and/or documentation with
        commercial products without prior permission.  An exception is
        granted to not-for-profit user's groups, which are authorized to
        charge a small fee (not to exceed $7) for materials, handling,
        postage, and general overhead.  NO FOR-PROFIT ORGANIZATION IS
        AUTHORIZED TO CHARGE ANY AMOUNT FOR DISTRIBUTION OF COPIES OF
        THE SOFTWARE OR DOCUMENTATION, OR TO INCLUDE COPIES OF THE
        SOFTWARE OR DOCUMENTATION WITH SALES OF THEIR OWN PRODUCTS.

        THIS INCLUDES A SPECIFIC PROHIBITION AGAINST FOR-PROFIT
        ORGANIZATIONS DISTRIBUTING THE SOFTWARE, EITHER ALONE OR WITH
        OTHER SOFTWARE, AND CHARGING A "HANDLING" OR "MATERIALS" FEE OR
        ANY OTHER SUCH FEE FOR THE DISTRIBUTION.  NO FOR-PROFIT
        ORGANIZATION IS AUTHORIZED TO INCLUDE THE SOFTWARE ON ANY MEDIA
        FOR WHICH MONEY IS CHARGED.  PERIOD.

        There is no restriction on the use of this software in
        commercial or institutional environments.

        No copy of the software may be distributed or given away without
        this document; and this notice must not be removed.

        There is no warranty of any kind, and the copyright owner is not
        liable for damages of any kind.  By using this free software,
        you agree to this.

        The software and documentation are:

                    Copyright (C) 1986, 1987, 1988, 1990 by
                            Christopher J. Dunford
                            The Cove Software Group
                                 P.O. Box 1072
                           Columbia, Maryland 21044

                                (301) 992-9371
                        CompuServe 76703,2002 [IBMNET]