SwapIRQ

                                   User Guide


                    Computer Telecommunication Systems, Inc.
                         3847 Foxwood Road, Suite 1000
                           Duluth, Georgia 30136-6100
                            Orders: 1-800-380-2666
                             Voice: 1-770-263-8623
                               FAX: 1-770-263-0124
                             Email: 76662.2315@compuserve.com


    (C) Copyright 1993-1995 Computer Telecommunication Systems, Inc.
    All Rights Reserved

    No part of this User Guide may be reproduced, transmitted, transcribed,
    stored in a retrieval system, or translated into any language (natural
    or computer), in any form or by any means, without the prior written
    permission of Computer Telecommunication Systems, Inc.

    Information in this manual is subject to change without notice and does
    not represent a commitment on the part of Computer Telecommunication
    Systems, Inc

    Computer Telecommunication Systems, Inc. may make improvements and/or
    changes in the manual and/or in SwapIRQ at any time

    Trademarks and Copyrights
    -------------------------
    IBM(R) and PS/2(R) are registered trademarks of International Business
    Machines Corporation.

    Hayes(R) is registered trademark of Hayes Microcomputer Products, Inc.

    The CTS Serial Port Utilities(TM), IRQInfo and SwapIRQ(TM) are
    trademarks of Computer Telecommunication Systems, Inc.




                               TABLE OF CONTENTS

        Introducing SwapIRQ. . . . . . . . . . . . . . . . . . . . . 1

        Installing SwapIRQ . . . . . . . . . . . . . . . . . . . . . 2

        Before Using SwapIRQ . . . . . . . . . . . . . . . . . . . . 2

        Using SwapIRQ. . . . . . . . . . . . . . . . . . . . . . . . 3
              Help Screen. . . . . . . . . . . . . . . . . . . . . . 3
              Loading SwapIRQ. . . . . . . . . . . . . . . . . . . . 3
                   Format 1: SwapIRQ /ih /is . . . . . . . . . . . . 3
                   Format 2: SwapIRQ /ih /is /n /M . . . . . . . . . 4
                   Format 3: SwapIRQ /ih /is /Aaaa /M. . . . . . . . 4
              Stopping SwapIRQ . . . . . . . . . . . . . . . . . . . 5
              Running SwapIRQ From a Batch File. . . . . . . . . . . 5

        Using SwapIRQ with Windows . . . . . . . . . . . . . . . . . 5

        Examples . . . . . . . . . . . . . . . . . . . . . . . . . . 6
              Example 1: Your modem is on Com3 using IRQ 5, but
                         software only uses Com3 with IRQ 4. . . . . 6
              Example 2: Your serial ports support high IRQs, but
                         your software doesn't . . . . . . . . . . . 6
              Example 3: Your modem is on Com3 using IRQ 5, and
                         your mouse is on Com1 using IRQ 4. Your
                         software uses Com3 on IRQ 4, which
                         conflicts with your serial mouse (also
                         using IRQ 4). . . . . . . . . . . . . . . . 7

        Appendix A: Conventional IRQ and Address
              Assignments for Serial Ports . . . . . . . . . . . . . 8

        Appendix B: Using SwapIRQ with Games . . . . . . . . . . . . 9

        Appendix C: Compatibility list . . . . . . . . . . . . . .  10



    Introducing SwapIRQ(TM)
    -----------------------
    SwapIRQ is a powerful but tiny DOS utility which allows your
    existing communications software to use any interrupt (IRQ)
    supported by your serial port or modem. You can also use it in a
    "DOS session" under Windows to provide access to an IRQ not
    supported by a DOS application. SwapIRQ works under DOS versions 2.0
    and higher, and uses less than 1K (actually, less than 800 bytes) of
    memory.

    Serial cards and board modems in your computer system are installed
    at a particular address and use an IRQ (an Interrupt ReQuest line)
    to signal the controlling software that they require attention. Some
    cards only allow selection of a Com port: Com1, Com2, etc., and use
    the industry standard addresses and IRQs as described in Appendix A.
    Other serial ports let you independently select a port address and
    IRQ which do not follow any particular standards.

    Communication software requires two pieces of information to work
    with a serial card or a board modem. First, software must know the
    address used by the board so that commands can be issued. Secondly,
    the software must know which IRQ is used by the board to request
    attention. Finally, you must be able to configure the software to
    use the address and IRQ used by the serial card. Otherwise, the
    board or modem will not work with the software.

    Communication software normally lets you select the port to use -
    Com1, Com2, and so on. A few applications are limited to using the
    two "standard" serial ports: Com1 at address 3F8H (hexadecimal) with
    IRQ 4, and Com2 at address 2F8H with IRQ 3. There are some serial
    ports that allow Com1 and Com2 to use other IRQs, and SwapIRQ will
    allow these applications to work with the ports on other IRQs.

    Other applications allow you to use more serial ports - Com3 and
    Com4 are common. However, many of these applications may require
    that the IRQ used by Com3 and Com4 are the same as the IRQs used by
    Com1 and Com2. SwapIRQ enables these applications to use Com3 and
    Com4 (or any serial port) on any available IRQ supported by the
    serial port.

    SwapIRQ does this by "redirecting the interrupt". For example, let's
    say that your software is set up to use Com3 on IRQ 4, but your
    serial port is set up as Com3 using IRQ 5. When your board generates
    the interrupt request (IRQ 5), your software won't see it because it
    isn't watching the correct IRQ (it's looking for IRQ 4). The result
    is a "hung application", or worse, a system lockup.

    But if you install SwapIRQ before using the application, then
    SwapIRQ "watches for" IRQ 5 for your application. When your serial
    board activates IRQ 5, SwapIRQ detects it and signals the IRQ your
    software uses (IRQ 4, in this case) that the interrupt occurred.
    This allows the software to operate normally. When you are finished
    with the application, you unload SwapIRQ to put your system back in
    its normal state.


                                      -1-


    Installing SwapIRQ
    ------------------
    SwapIRQ is normally placed in a subdirectory on your hard disk. The
    following instructions assume you will put SwapIRQ in a directory
    named "SWAPIRQ":

      1.  Create an "SWAPIRQ" subdirectory on your hard disk
          using the DOS Make Directory (MD) command:

          Example: C>MD SWAPIRQ <Enter>

          NOTE: <Enter> means to press the Enter (Return) key.

      2.  Change the default directory to the directory you
          created using the DOS Change Directory (CD)
          command:

          Example: C>CD SWAPIRQ <Enter>

      3.  Copy the distribution files to the SWAPIRQ directory. If
          the distribution files are on a floppy diskette in drive A,
          you would enter:

          Example: C:\SWAPIRQ>COPY A:\*.* <Enter>

    If your directory contains a README.TXT file, then check this file
    for additional information not included in this User Guide.

    SwapIRQ is ready to run. To make SwapIRQ available to all of your
    applications, you can add the SwapIRQ directory to the PATH command
    in your AUTOEXEC.BAT file. An alternative is to use a batch file for
    each of your applications requiring SwapIRQ as described on Page 8.


    Before Using SwapIRQ
    --------------------
    Before you use SwapIRQ with your serial ports, you should verify
    that your system has no serious serial port or interrupt conflicts.
    If you have been using your current system for some time without
    problems, then you can probably assume that your system is
    configured properly. If you have changed your system setup recently,
    or if you have occasional difficulties, then a little additional
    testing is worth the effort. If you have the CTS Serial Port
    Utilities, then run PortInfo, paying careful attention to the error
    and warning messages regarding port and interrupt conflicts. If
    PortInfo detects serial port conflicts, then these should be
    resolved before using SwapIRQ.

    If you do not have the CTS Serial Port Utilities, then we suggest
    you contact us to obtain a copy, particularly if you observe any
    problems with SwapIRQ.

    After you have verified that your system is in good working order,
    then you need to determine which interrupt your hardware is
    generating, and which interrupts your software can use. You will use
    this information when starting SwapIRQ.


                                      -2-


    Using SwapIRQ
    -------------
    SwapIRQ is a TSR application that you load before running your
    application which requires the special interrupt handling, and
    unload when you are finished. SwapIRQ is controlled through command
    line switches, and is aware of CTSCOMn environment variables. There
    are several possible command lines formats:

    Help Screen

        You can display the help screen from the DOS prompt by entering
        either:

          C:\SWAPIRQ>SwapIRQ <Enter>

          -OR-

          C:\SWAPIRQ>SwapIRQ /? <Enter>

    Loading SwapIRQ

        There are three formats for loading SwapIRQ. The first is fine
        to use under most circumstances. However, if you experience
        problems with SwapIRQ when using the first format, then try the
        second. The second format will make sure that another serial
        port will not generate interrupts that conflict with SwapIRQ.
        You can even completely disable a serial mouse that uses the
        same IRQ required by your software for something else!

    Format 1: SwapIRQ /ih /is

        This command installs the SwapIRQ program, and swaps hardware
        IRQ 'h' to software IRQ 's'. That is, the serial port is using
        IRQ 'h' to signal the software, which is looking for IRQ 's'

          where:'h' is the IRQ generated by the hardware
               's' is the IRQ expected by the software

          NOTE: They must be in the sequence shown.

          The valid 'h' and 's' values are decimal 2-7 for an IBM PC/XT
          computer, and 3-7, 9-12, 14 and 15 for an IBM AT or compatible
          machine.

          NOTE: if your board has a setting for IRQ 2, it is actually
          using IRQ 9 in an IBM AT or compatible computer. You should
          use IRQ 9 as the hardware IRQ. You can use IRQ 2 as the
          software IRQ.


                                      -3-


        For example, using the command line:

          SwapIRQ /i5 /i4

        SwapIRQ will translate IRQ 5 generated by the serial port to IRQ
        4 for the software.

    NOTE: There is one important limitation when using SwapIRQ. The
    "software interrupt" cannot be used by a hardware device at the same
    time that SwapIRQ is in use. In the example above, the IRQ 4 line
    must be dedicated to SwapIRQ. The Com1 serial port, which normally
    uses IRQ 4, must be inactive while SwapIRQ is loaded. See command
    Format 2 on how to disable interrupts from a serial port or serial
    mouse while SwapIRQ is loaded.

    Format 2: SwapIRQ /ih /is /n /M
          where 'n' is a valid serial port number of 1-8. The '/n'
          switch instructs SwapIRQ to disable interrupts from serial
          port 'n'. Use this switch if you are switching a hardware
          interrupt over to an interrupt line used by another serial
          port. This will prevent a stray interrupt from the serial port
          from contesting with the swapped interrupt.

          If you add a '/M' switch to the command line, this will
          completely disable a serial mouse on port 'n'. Applications
          that use a mouse may require this command format to run
          correctly with SwapIRQ.

          NOTE: If you use the CTS Serial Port Utilities and the CTSCOMn
          environment variables, then SwapIRQ will use these port
          assignments.

    Format 3: SwapIRQ /ih /is /Aaaa /M
          where 'aaa' is a valid serial port address, in hexadecimal.
          You can use this option to disable interrupts from a serial
          port at address 'aaa'. Use this command if you are swapping a
          hardware IRQ over to an IRQ line used by a non-standard serial
          port, and you do not have a CTS Serial Port Utility CTSCOMn
          environment variable defined for the port.

          The '/M' switch behaves just as described above.


                                      -4-


    Stopping SwapIRQ

        Stop SwapIRQ from running when you have finished with the
        application that needs it. This is done with the command:

         C:\SWAPIRQ>SwapIRQ /D <Enter>

        This command removes SwapIRQ from memory and restores all
        interrupt control back to a normal status. If another
        application has been loaded since SwapIRQ was installed, then
        SwapIRQ will only be disabled and not removed from memory. In
        this case, you will lose about 1K of system memory until your
        next system startup (reboot).

    NOTE: it is recommended that you load SwapIRQ just before running
    your application and then unload it immediately afterwards. You can
    put the SwapIRQ commands into a batch file to automate the process.

    Running SwapIRQ From a Batch File

        You can set up batch files to automatically load and unload
        SwapIRQ by doing the following (this assumes that SwapIRQ is
        located in a directory SWAPIRQ on the "C" drive):

        Create a batch file in the directory of the program that
        requires SwapIRQ that starts SwapIRQ, then runs the
        communication application you need, and then unloads SwapIRQ
        when you have finished.

        FILE: SAMPLE.BAT

              c:\SWAPIRQ\SwapIRQ /i5 /i4  (to swap IRQ 5 to IRQ 4)

              CommProg       (put the program startup string here)

              c:\SWAPIRQ\SwapIRQ /d       (unloads SwapIRQ)

    Using SwapIRQ with Windows
    --------------------------
    You can use SwapIRQ in Windows just like you do in DOS. Before using
    SwapIRQ with Windows, it is important to have Windows properly
    configured for the serial ports you have in your system. You can do
    this either through your Windows control panel, or by editing the
    WIN.INI file with a text editor. See your Microsoft Windows
    documentation for additional information.

    You use SwapIRQ under Windows in a DOS box to provide access for
    DOS-based communication applications to IRQs not supported directly
    by the application. Load SwapIRQ as a described for DOS in a Windows
    DOS box before running your DOS communications program. Then run the
    application just as you would under DOS.


                                      -5-


    Examples
    --------
    Example 1: Your modem is on Com3 using IRQ 5, but software only uses
    Com3 with IRQ 4

    You have a modem on Com3, IRQ 5. Most of your software supports this
    modem. However, one application allows use of Com3, but won't let
    you specify the IRQ used by the port.

    Solution: Use SwapIRQ to "redirect" IRQ 5 generated by the modem to
    IRQ 4 (the conventional IRQ for Com3) when using this application.
    To be on the safe side, you also disable Com1 from generating
    interrupts on IRQ 4 while SwapIRQ is loaded. You can do this with
    the command line "SWAPIRQ /i5 /i4 /1" where:

          SwapIRQ /i5 /i4 /1
                    ^   ^  ^
                    |   |  |
                    |   |  +---- Disable Com1 IRQs (Com1 uses IRQ 4)
                    |   |
                    |   +------- The software uses IRQ 4
                    |
                    +----------- The modem uses IRQ 5

    Com1 is now disabled until you unload SwapIRQ or until another
    application re-enables it. Run your application that needed the
    interrupts swapped. When you are finished with the application, you
    unload SwapIRQ to restore your system to a "normal" status.

    Example 2: Your serial ports support high IRQs, but your software
    doesn't:

    You have a 16-bit serial board that supports high IRQs (10-12, 14
    and 15), but some of your software doesn't allow you to access these
    IRQs.

    Solution: Use SwapIRQ to redirect the high IRQs to the conventional
    IRQs supported by most communication software. For example, if you
    need to use Com4, IRQ 11 with an application that expects Com4 to
    use IRQ 3, then you load SwapIRQ before running the application with
    the command:

          C:\SWAPIRQ>SwapIRQ /i11 /i3 <Enter>

          - OR -

          C:\SWAPIRQ>SwapIRQ /i11 /i3 /2 <Enter>
          (to prevent Com2 from generating interrupts on IRQ 3)

    NOTE: the command line "switches" like "/i", "/a", and "/d" can be
    either uppercase or lowercase letters.


                                      -6-



    Example 3: Your modem is on Com3 using IRQ 5, and your mouse is on
    Com1 using IRQ 4. Your software uses Com3 on IRQ 4, which conflicts
    with your serial mouse (also using IRQ 4).

    Solution: You use SwapIRQ to get access to the modem on IRQ 4 and to
    prevent the mouse from interfering.

    NOTE: you will not be able to use the mouse in this application,
    since SwapIRQ shuts off the mouse!

    To do this, you load SwapIRQ with the command:

         SwapIRQ /i5 /i4 /1 /M
                   ^   ^  ^  ^
                   |   |  |  |
                   |   |  |  +------- Disables the mouse
                   |   |  |
                   |   |  +---------- Disables IRQs from Com1
                   |   |              (which uses IRQ 4)
                   |   |
                   |   +------------- The software uses IRQ 4
                   |
                   +----------------- The modem uses IRQ 5

    Then run your application. When you are finished with your
    application, stop SwapIRQ. Your mouse will be available to the next
    application you use after stopping SwapIRQ.


                                      -7-


    Appendix A: Conventional IRQ and Address Assignments for Serial Ports

      I. ISA (IBM AT and Compatible) Computers

    Serial Port    IRQ        Address (first address, in hexadecimal)
       Com1         4         3F8   (this is a STANDARD!)
       Com2         3         2F8   (this is a STANDARD!)
       Com3         4         3E8   (a convention)
       Com4         3         2E8   (a convention)

    NOTE: there are no conventions for Com5 or higher.


    II. Microchannel Architecture (IBM PS/2) Computers

    Serial Port    IRQ        Address (first address, in hexadecimal)
       Com1         4         3F8
       Com2         3         2F8
       Com3         3         3220
       Com4         3         3228
       Com5         3         4220
       Com6         3         4228
       Com7         3         5220
       Com8         3         5228

    NOTE: These are standards as defined by IBM.


                                      -8-


    Appendix B: Using SwapIRQ with Games

    Many DOS games are set up to only work with one IRQ - usually IRQ 5
    or IRQ 7. If your sound card is not set up to work on that IRQ, you
    miss all of the sound. While SwapIRQ was developed specifically for
    communications, you can use it with many DOS games to allow the
    sound card IRQ to get through to the game software.

    Operation with games is similar to that for communication software.
    Simply replace the word "modem" with "sound card" in all earlier
    sections of the User Guide.

    Example 4: Your sound card uses IRQ 5, but the game software
    requires the sound card on IRQ 7:

    Solution: Use SwapIRQ to "redirect" IRQ 5 generated by the sound
    card to IRQ 7.

          SwapIRQ /i5 /i7
                    ^   ^
                    |   |
                    |   +------- The game software uses IRQ 7
                    |
                    +----------- The sound card uses IRQ 5


                                      -9-



    Appendix C: Compatibility List

    SwapIRQ has been used extensively for over 2 years with a wide range
    of communications software. At the time of this initial shareware
    release, the only known incompatibilities are with the America
    Online for DOS and Prodigy for DOS programs.

    I would like to compile a list of games that do and do not operate;
    please let us know how SwapIRQ works for you by contacting us via
    any means listed on the title page of this User Guide.


    Association Of Shareware Professionals Member
    =============================================

                  _______
             ____|__     |                (R)
          --|       |    |-------------------
            |   ____|__  |  Association of
            |  |       |_|  Shareware
            |__|   o   |    Professionals
          -----|   |   |---------------------
               |___|___|    MEMBER


    This program is produced by a member of the Association of
    Shareware Professionals (ASP). ASP wants to make sure that the
    shareware principle works for you. If you are unable to resolve a
    shareware-related problem with an ASP member by contacting the
    member directly, ASP may be able to help. The ASP Ombudsman can
    help you resolve a dispute or problem with an ASP member, but
    does not provide technical support for members' products.  Please
    write to the ASP Ombudsman at 545 Grover Road, Muskegon, MI
    49442-9427 USA, FAX 616-788-2765 or send a CompuServe message via
    CompuServe Mail to ASP Ombudsman 70007,3536.


                                      -10-



  Name: ______________________________        Telephone: ____________________

  Company: ________________________________   E-mail ID: ____________________

  Address: __________________________________________________________________

           __________________________________________________________________

   QTY   Description                               Price           Subtotal
   ===   ===========                               =====           ========
   ___   SwapIRQ with on-disk User Guide             $20           ________
   ___   SwapIRQ with Printed User Guide             $24           ________

 Other Products (special prices valid only with SwapIRQ order):
 (see the descriptions and in PRODUCTS.DOC)

   ___   IRQInfo ....... Normally $28.95 - only ....  24           ________
   ___   IRQInfo PRO ... Normally $41.95 - only ....  35           ________
   ___   PortFix ....... Normally $14.95 - only ....  10           ________

   ___   The CTS Serial Port Utilities
         (see the description and the order form in PRODUCTS.DOC)

   ___   The CTS Modem Utilities
         (available soon - call or write for details)
                                                                   ========

                                                    Sub-Total     $________

         Sales Tax:                  Georgia residents add 5%     $________

         Shipping & Handling:                                     $    4.00
                                                                  =========

                                     TOTAL (US dollars, please)   $________

 PAYMENT METHOD:  Check __    Money Order __    EuroCheq __     Discover __
  Visa __    MasterCard __    Am. Express __    Purchase Order ($50 min) __
   ========================================================================
                            CREDIT CARD INFORMATION

       Name as it appears on the card: _________________________________

       Card No. ________  ________  ________  ________  Expires  ___/___

       Cardholder signature: ___________________________________________

   Please send, FAX, email or call:
     +-------------------------------------------------------------------+
     |              Computer Telecommunication Systems, Inc.             |
     |                   3847 Foxwood Road, Suite 1000                   |
     |                   Duluth, Georgia  30136-6100 USA                 |
     +------------------------------+------------------------------------+
     |           Telephone          |          Electronic Mail           |
     |           ---------          |          ---------------           |
     |       Orders: 1-800-380-2666 |       CompuServe: 76662,2315       |
     |        Voice: 1-770-263-8623 | Internet:76662.2315@compuserve.com |
     |          FAX: 1-770-263-0124 |                                    |
     +------------------------------+------------------------------------+
 NOTE: Federal TaxID: 58-1880693. Prices are subject to change without
 notice.