NOVELL TECHNICAL INFORMATION DOCUMENT (03/03/95)                

DSREPAIR.DOC for DSREPAIR.NLM version 2.21 for NetWare 
4.0x Servers

The DSREPAIR.NLM file version 2.21 for NetWare 4.0x 
servers includes an enhancement that allows for editing replica
rings and printing information about the local database (DIB). 
This document provides you with procedures and examples for
determining when and how to use these enhancements.

This document contains important information that is not included
in the NetWare 4.0x manual set or online Help or in the NetWare
4.0x release notes.

The following table of contents is provided for this document:
 
I. Updating the DSREPAIR.NLM File to Version 2.21
     II. Using the DSREPAIR Utility 
          A. Using the Select Options
          B. Beginning the Repair Process
          C. Saving Replica Ring Information
          D. Checking Server Addresses
          E. Checking IDs In a Remote ID Table
          F. Checking Remote IDs In Replica Rings
          G. Moving NetWare 4.0x Servers to the Correct Tree
          H. Verifying Backlinks and External References
     III. Using the DSREPAIR Utility to Edit the Replica Rings
           A. Using the Ring Repair Menu
               1. Changing the Replica Type of a Server Replica
                  to the MASTER 
               2. Editing the Replica Ring for a Partition
           B. Example of Repair Method

================================================================

I. Updating the DSREPAIR.NLM File to Version 2.21

The DSREPAIR.NLM file version 2.21 is included in this package.
This utility is supplied in an English-only version. You should
copy the DSREPAIR.NLM file to all NetWare 4.0x servers that will
run the DSREPAIR utility.

     Prerequisites

     Access to the server console or Supervisory rights to the
     SYS:SYSTEM directory.

     Procedure 

    1. COPY the DSREPAIR.NLM file to the SYS:SYSTEM directory on
       every NetWare 4.0x server that you want to run the 
       utility. 


II. Using the DSREPAIR Utility 

The DSREPAIR console command utility is provided with NetWare 
4.0x software to repair problems with NetWare Directory Services
(NDS) on a single-server basis. It does not correct problems on
other servers from a single, centralized location. It must be 
run on each server that you want to correct Directory database
errors on. 

IMPORTANT: DSREPAIR affects only the parts of the database 
stored on the server where you run it. To fix the entire 
database, you must run the utility on each server which contains
a part of the database.

This utility checks and repairs the partitions and replicas 
stored on the server where you run it. The utility also checks
and repairs NDS records, schema, bindery objects, and external
references.

Some NDS database problems are not fatal, and NDS continues to
operate. But if the database becomes corrupted, you get a 
message on the console that the server could not open the local
database. In this case, run DSREPAIR or reinstall the NDS 
database to fix the problem so that the database can be opened.

     Procedure

     1. At the server console prompt, run DSREPAIR by typing
        dsrepair <Enter>

        The utility locks the database and displays the 
        following menu options:

        1)Select Options           View current DSREPAIR 
                                   settings and select options
                                   from the following table. 
                                   (When an option is on, an
                                   asterisk appears at the left
                                   of the option.)

        2)  Begin Repair           Starts the repair process.

        3) Save Replica Ring       Allows you to save the
           Information             replica ring information
                                   that you changed in the 
                                   replica ring editor. 

        4)Check Server Addresses   Checks the network address 
                                   of every server known to this
                                   server with an address from 
                                   SAP and verify that the 
                                   network address is correct. 

        5) Check IDs In Remote    Checks the remote server ID
           ID Table                table and repair it. 

        6) Check Remote IDs In     Contacts each server in each
           Replica Rings           partition root's replica ring
                                   for every partition root on 
                                   this server.
                                                                  
        7) Move This Server To     Assists NetWare 4.01 and 
           The Correct Tree        NetWare 4.02 servers to
                                   identify the correct tree
                                   they reside in after a tree
                                   merge or tree name rename
                                   operation using the 
                                   DSMERGE.NLM.

        8) Verify Backlinks and    Prepares a NetWare 401 or
           External References     NetWare 4.02 server for
                                   upgrading to Netware 4.1.


     A. Using the Select Options

     The Select Options allows you to configure DSREPAIR for 
     your particular environment and repair needs. Each option
     has an active and inactive function that you can select. 
     You toggle between the active or inactive function for 
     each option by typing the letter that corresponds with the
     option. An astrick (*) is placed by the left side of each
     option when activated.

     The following table list and defines the available options:

     Option 1) Pause after each error/
               Do not pause after each error 

               Cause DSREPAIR to pause after each error.

     Option 2) Unattended repair/
               Do not exit automatically upon completion 

               Causes DSREPAIR to operate in unattended mode
               (DSREPAIR runs and exits without intervention).
               You can also set this option by using the -U 
               switch on the command line.

     Option 3) Log errors to a file/
               Do not log errors to a file 

               Designates a file where errors are logged. 
               (Default: SYS:SYSTEM\DSREPAIR.LOG.) (You can 
               also specify a file by using the -L log_filename
               on the command line. Turn this option off if you
               don't want to log errors.)

     Option 4) New Replica Ring Editor Feature/
               Do not repair replica ring 

               Causes DSREPAIR to display the Replica Repair 
               Menu. See "Using the DSREPAIR Utility to Edit the
               Replica Rings" for more information.

     Option 5) Check for valid mail directories/
               Do not check for valid mail directories 

               Causes DSREPAIR to check SYS:MAIL for 
               subdirectories that must have the name of user 
               IDs in the NDS database. If an object 
               with the ID of the directory name does not exist,
               the mail directory with that ID is removed.

     Option 6) Check file system for valid trustee IDs/
               Do not check file system for valid trustee IDs

               Causes DSREPAIR to check the file system for 
               valid trustees. DSREPAIR makes sure that every
               ID in the file system has a corresponding valid
               ID in the NDS database. If not, the ID is purged
               from the database. This operation might take
               considerable time, depending on the size and 
               number of volumes.

     Option 7) Check for valid stream files/
               Do not check for valid stream files 

               Causes DSREPAIR to check for valid stream files.
               DSREPAIR checks the NDS secure file area for 
               valid stream files that must correspond to stream
               properties of objects. If not, the stream file is
               deleted.

     Option 8) Return to the main menu.


     B. Beginning the Repair Process

     The repair process uses the option settings made in the
     "Select Options" menu. If the DSREPAIR utility finds any
     correctable problems, the changes are made in a temporary
     file set.

     When checking is completed, a prompt appears asking you 
     if you want to save the temporary file set even if no 
     errors were reported. To save the database, select "Yes"
     at the prompt.

     If you save the changes, the "Invalid Trustee" check is
     performed on the mounted volumes. If trustee assignments
     exist for objects that have been deleted from the database,
     the trustee's rights are deleted from the file system.

     When the repair process is complete, the message "Repair
     process completed" appears.


     C. Saving Replica Ring Information
 
     Saving the replica ring information allows you to keep a
     record of all the servers within a particular replica ring.
     You can display or print out this information to a log file
     (Default filename is SYS:SYSTEM\DSREPAIR.LOG).


     D. Checking Server Addresses

     This option will check the network address of every server
     found in the database with an address from SAP (Service
     Advertising Protocol) and verify that the network address
     is correct. If an NCP_SERVER class object does not have a
     NETWORK_ADDRESS property, one will be added. 

     NDS servers advertise their presence to other servers using
     SAP packets which contain their name and address.

     If the address in incorrect, it will be replaced with the
     address from SAP. 

     Also, all replica rings are searched to find the server that
     the address is being verified for, and the address in the
     replica property is also checked. If the address is
     incorrect, a warning message is generated and displayed. 
     A future version of the DSREPAIR utility will repair the
     address in the replica property.

     NOTE: The local servers database is not locked while this
     operation is performed. 


     E. Checking IDs In a Remote ID Table

     This option checks the remote server ID table and 
     repairs it. 

     NOTE: The local servers database is not locked while this
     operation is performed. 

     The remote server ID table contains a list of ID pairs.
     The first ID (local ID) is the ID of a server in the 
     Directory tree. The second ID (remote ID) is the ID of 
     the server you are running DSREPAIR on as it exists in 
     the remote server's database. 
     
     Because ID numbers are specific and unique to each server,
     the ID of the server in another server's database will
     probably be different for every server. This server
     identifies itself to other servers by using the ID from
     the other servers' local database.

     If DSREPAIR cannot connect to the other server (identified
     in the local database by the Local ID) then no further
     checking is performed. 

     If a server no longer exists in the tree, then the server
     object for that server should be deleted. Any external
     references to the server object it are purged when the
     backlink process cannot resolve the object. This may take 
     one or two days' time to resolve.

     As the server object and the external references to it are
     deleted, the local server ID is deleted from the table.
     If the deleted servers persist in the ID list, there is 
     some other problem causing the ID checking to fail. If the
     server is down, then it will be checked later if the 
     repair is run again when the server is back online. 

     DSREPAIR will verify that the remote ID is correct and 
     then read the remote servers public key, and authenticate
     to the remote server. If the remote server's object is an
     external reference on the remote servers database, then it
     will report error -631 reading the public key. This is 
     because you cannot read a property of an external reference
     remotely. Therefore, this is not a problem. The connection
     should still authenticate. If the authentication fails, 
     then there is a damaged key somewhere within the tree. 
     This will be addressed in a future release of DSREPAIR. 

     If the remote ID resolves to a server other than this one
     in the remote database, it may be because a rename or move
     has occurred and the Distinguished Name of this server has
     changed on the other server. 

     If the remote ID does not seem to be this server's remote
     ID, DSREPAIR attempts to resolve this server's name on the
     remote server and put the correct ID in the remote ID 
     table. If the server can authenticate, then the procedure 
     worked and the table has been repaired.

     If the local ID cannot be resolved in the local database,
     then the ID pair is deleted. 

     F. Checking Remote IDs In Replica Rings

     This option will contact each server in the partition
     root's replica ring. This is done for every partition 
     root on this server. 

     NOTE: The local servers database is not locked while this
     operation is performed. 

     The replica property contains an ID (local ID) for a remote
     server and the ID (remote ID) of the partition root in that
     server's database. 

     DSREPAIR will verify that the remote partition ID is valid
     and if it is not, it will try to repair the remote ID or
     delete the server from the replica ring. 

     G. Moving NetWare 4.0x Servers to the Correct Tree

     When a tree merge or tree rename operation is performed
     in a Netware 4.1 Directory tree that contains servers 
     running NetWare version 4.01 and 4.02, you might need to
     identify the correct tree on the NetWare 4.0x servers after
     the operation is completed.

     If a NetWare 4.02 server is up and can communicate the 
     NetWare 4.1 server that is running DSMERGE, then the 
     tree should rename properly on the NetWare 4.02 server. 

     If a 4.01 server is in the tree, it will rename its tree
     name, and then it will stop communicating with other 
     servers. 

     To resolve this, down the server and bring it up again,
     or run this DSREPAIR and select the "Begin Repair" option
     to repair the local database. 

     If either the 4.01 or 4.02 server is down during a rename 
     tree or a merge tree operation, they will not be able to
     change their tree name when they are booted again. This 
     only affects the servers in the source tree during a merge
     tree since servers in the target tree do not change their 
     tree name during a merge. The source tree is the one that 
     the DSMERGE.NLM is running on.

     To fix servers running NetWare 4.0x that cannot find the
     correct tree name after they are brought back up, run the
     "Moving NetWare 4.0x Servers to the Correct Tree" option. 
     A list of all the tree names found in SAP are displayed. 

     You should then select the tree that the server belongs to.
     You are then asked to login to the tree to verify that you
     have rights to perform this operation. Login as the ADMIN
     user or a user that has similar rights. Then the server
     attempts to authenticate to the tree, and if this is
     successful, the tree name for the server is changed. 

     H. Verifying Backlinks and External References

     This option is used to check a Directory database before
     upgrading a NetWare4.01 or NetWare 4.02 server to 
     Netware 4.1. 

     External references are local place holders for objects
     that reside in partitions stored on other servers in the
     Directory tree. These external reference objects are 
     required locally because they have been referenced by the
     file system or an object in a local partition. 

     Backlinks are pointers on local objects to servers that
     contain an external reference of that object. NDS maintains
     the backlinks and external references, and typically 
     removes them when they are no longer needed. There are 
     occasions however that these items either have not yet been
     removed or have failed to be removed. 

     External references and their associated real objects on
     another server can have different creation time stamps. 
     This is not abnormal behavior in Netware 4.01 and 
     NetWare 4.02 environments. 

     Netware 4.1 however uses these timestamps differently and
     requires an external reference and the actual object to 
     have identical creation time stamps. 

     This option examines the local database integrity with 
     regard to external references and backlinks and removes
     them when possible. Any timestamp mismatch is recorded in
     the DSREPAIR.LOG file. This option should be used and the
     log file examined to be sure there are no problems reported
     in the local database before upgrading to Netware 4.1. 


III. Using the DSREPAIR Utility to Edit the Replica Rings 

     The DSREPAIR utility version 2.21 allows you to resolve
     errors that occurred because the MASTER replica for
     a partition is lost or a server within a specific 
     replica ring no longer exists in the Directory tree. The
     errors occur primarily during partitioning operations such
     as join and split.

     Use the DSREPAIR utility at the system console prompt to
     designate a MASTER replica and edit the replica rings for a
     partition.

     
     Procedure

     1. At the server console prompt, run DSREPAIR by typing

        dsrepair <Enter>

     2. To set options for editing the replica ring, type "1".

     3. Select "New Replica Ring Editor Feature" option by
        typing number "4."

     4. Select option "8" to return to the main menu.

     5. At the main menu screen, type "2" to begin checking
        the database.

        Changes are saved in a temporary file set until all of
        the partitions and replicas on the server are checked. 

        Following the local database repair, the "Ring Repair
        Menu" appears if replicas exist on the server.


     A. Using the Ring Repair Menu

     The "Ring Repair Menu" displays a list of all replica root
     objects stored on the server. The list may include the
     following replica types:

     MASTER
     SECONDARY
     READ-ONLY
     SUBORDINATE

     Each replica is assigned a unique number which appears on
     the left side of the screen. You should record the unique
     number that corresponds to the replica that you want 
     to edit.

     If more replicas are found than can be displayed on the
     first screen, you will be prompted to press a key to see
     the next screen until the list is completely displayed.

     When the list is complete, you are prompted to select a
     replica by typing in the unique number of the replica,or
     type "0" (zero) to exit and continue with the repair. 

     When you select a replica, the following options appear:

     1)   Change Replica Type to Master
     2)   Edit Replica Ring 

     
     1. Changing the Replica Type to MASTER

        Changing a replica type to a MASTER is used to select
        a new MASTER replica for a partition that has lost the
        MASTER replica. 

        You can lose a MASTER replica by

        - Uninstalling the server containing the MASTER replica
          from the Directory tree.

        - The server containing the MASTER replica is damaged or
          destroyed. 

        Without a MASTER replica, partition operations such as
        split and join cannot be performed. This is because all
        workstation utilities that perform partition operations
        contact the MASTER replica of a partition first to
        schedule these operations. 

        The replica contained on the server you are running the
        DSREPAIR utility will be changed to the new MASTER
        replica for a particular partition if the servername
        exists in the replica ring for that partition. If you
        want to set some other server that has a replica of the
        partition as the server containing the MASTER replica,
        you should run DSREPAIR on that server. 

        The following conditions exist for changing replicas to
        the MASTER replica for:

        SECONDARY or READ-ONLY

             You should change only SECONDARY or READ-ONLY
             replicas become a MASTER replica.

             If another server is found in the replica ring
             that contains the MASTER replica for a given
             partition, it is changed to a SECONDARY. 

             If the server that originally contained the MASTER
             replica is reintroduced into the Directory tree
             (comes back on line), the new replica ring with the
             new MASTER replica information will over-write the
             old one. The original server that contained the
             MASTER replica is changed to contain a SECONDARY 
             partition in the replica ring table.

        SUBORDINATE

            Only in the case of a complete loss of all replicas
            (MASTER, SECONDARY, READ-ONLY) for a given 
            partition, should you change a SUBORDINATE replica
            to a MASTER.

            SUBORDINATE replicas exist as reference partition
            roots for the partition; however, these are not
            real replicas of the partition. 

            Because SUBORDINATE replicas are only reference
            points, there are no copies of the objects, their
            properties, or their data left in the Directory
            tree. 

            There may however be external reference objects
            subordinate to the SUBORDINATE reference partition
            roots that contain the names of the objects. These
            external reference objects were created on these
            servers because they needed object IDs to grant
            rights to the file system for these objects. 

            You will be able to see the partition with the
            workstation utilities; however, partition operations
            will fail, and when you try to view the servers that
            contain replicas of the partition, none will be
            displayed. This is because the workstation 
            utilities do not show servers with SUBORDINATE type
            partition roots. 

            When you select a SUBORDINATE replica to be changed
            to the MASTER, a message appears alerting you to run
            DSREPAIR again on this server. This is because the
            subordinate reference objects that were contained by
            the SUBORDINATE replica are now subordinate to a 
            MASTER replica. This is an illegal condition in the
            Directory database.

            When DSREPAIR runs again, it will change the 
            external reference objects to real objects with
            a base class of "unknown." Be aware that DSREPAIR
            generates a lot of errors on the objects in this
            replica when this takes place. 

            At this point, you have a MASTER replica of the
            partition, and it contains some but probably not all
            of the objects that were in the original replica.
            However, hese objects all have the object class of
            "unknown," and they have no properties or data.
            You can restore the replica from a tape drive with
            SMS, which restores all the properties and data for
            these objects, or to clean up the tree, delete all
            the objects in the replica. Then join the partition
            root object with the parent partition, which changes
            the object from a partition root to just a
            container, and then delete the container object. 

            When the deletion is complete, you are returned to
            the list of replicas. You can select another replica
            and perform the operation again. 

            Selecting "0" (zero) returns you to the main repair
            screen. 

            When the change is completed, a prompt appears
            asking you if you want to save the changes.

            Decide if you want to make changes to the database.

            To change the database, select "Yes" at the prompt.

            If you save the changes, the utility then does an 
            "Invalid Trustee" check on the mounted volumes. If
            trustee assignments exist for objects that have been
            deleted from the database, the trustee's rights are 
            deleted from the file system.

            When the repair process is complete, the message
           "Repair process completed" appears.


     2. Editing the Replica Ring for a Partition

        Editing the replica ring for a partition is primarily
        modifying a list of all the servers that contain a
        replica of a given partition. 

        You should edit the replica ring if any server
        containing a replica of a partition is uninstalled
        or does not exist in the Directory tree. Examples of
        this condition are as follows:

        - The server was properly removed from the Directory
          tree with the INSTALL.NLM utility. 

        - The server object was deleted; however, some
          references to the server object still exist because
          of tree or synchronization failures.

        - A server was physically damaged or removed from the
          tree without being uninstalled.

        These conditions will commonly generate the -625 error
        on the NDS server console when the SET DSTRACE=ON
        command is enabled. The -625 error prevents
        synchronization from completing properly because NDS
        attempts to updated all servers in a replica ring with
        the latest information. This error also prevents objects
        marked for deletion from being purged, because all 
        servers in a replica ring must be informed of a
        deletion.

        You should edit the replica ring and delete any server
        that no longer exists in the Directory tree. 

        When editing the replica ring, the following information
        is available:

        - A list of all servers that contain a replica are
          displayed

        - A unique number is assigned to each server

        - The type of replica on that is contained on a server
          for that partition

        - The servers Directory Name

        - The current status or the server in the replica ring
          ("Present" or "Deleted")

        You can delete a server from the replica ring by typing
        in the unique number that corresponds with the
        servername. After a server is deleted from the ring, it
        cannot be added again. 

        CAUTION: If you delete a server that still exists in the
        Directory tree, that server will no longer be
        synchronized with the Directory database. 

       If you make a mistake and delete the wrong server, exit
       the ring editor by selecting "0" (zero) at each prompt,
       and return to the main repair screen. When you are
       prompted to save the database (DIB), select "N" for NO
       and run DSREPAIR again to access the ring editor and make
       the correct selection. 

       You may want to check the ring of each replica on this
       server. This is the only way to be sure that the failed
       server has been removed from all replica rings. 

       When the deletion is complete, you are returned to the
       list of replicas. You can select another replica and
       perform the operation again. 

       Selecting "0" (zero) returns you to the main repair
       screen. 

       When checking is completed, a prompt appears asking you
       if you want to save the changes.

       Decide if you want to make changes to the database.

       To change the database, select "Yes" at the prompt.

       If you save the changes, the utility changes the
       database and then does an "Invalid Trustee" check on the
       mounted volumes. If trustee assignments exist for objects
       that have been deleted from the database, the trustee's
       rights are deleted from the file system.

       When the repair process is complete, the message "Repair
       process completed" appears.

       WARNING: If you remove a server from the replica ring
       that still has a replica of the partition, you will need
       to contact a Novell Technical Support representative to
       correct the problem.


     B. Example of Repair Method

     Problem: A Server that Was Not Properly Removed

     Scenario: The server SERV3-MASTER was deleted from the tree
               for several months but still appeared in the
               DETROIT partition ring on server SERV4-MASTER.
               The DS console screen on a server in the same
               partition is generating -625 errors.

     The DS console screen appears as follows:

          SYNC: Start sync of partition OU=DETROIT. 

          2D52D8D6:967 SYNC: Start outbound sync with server
          <CN=SERV1-> 

          2D52D8D6:239 SYNC: Start outbound sync with server 
          <CN=SERV2->

          2D52D8D7:052 SYNC: Start outbound sync with server 
          <CN=SERV3-> 

          2D52D90F:402 (16:23:59) SYNC: failed to communicate
          with server <CN=SERV3-> ERROR: -625 

          2D52D914:962   SYNC: End sync of partition OU=DETROIT.
          All processed = NO. 

     To remove SERV3-MASTER from the ring, you should complete
     the following steps:

     Procedure

     1. Run the DSREPAIR.NLM on SERV4-MASTER

     2. Select option 1 from the main menu for selection
        options.

     3. From the Selections Menu, choose option "4," "Repair
        replica ring with manual editor" by typing "4."

        You are returned to the Main Menu.

     4. Select Option 2 to start the repair process.

        After running DSREPAIR, the following screen appears:

        Replica Type Name 

        19     SECONDARY       "OU=UGH" 
        20     MASTER          "OU=DETROIT" 
        21     MASTER          "OU=FOO"
        22     SUBORDINATE     "OU=DOSFISH" 

     5. Choose the DETROIT partition ring by typing 

        20 <Enter>. 

        You can now change the replica on the server to the
        MASTER or modify the replica ring. This example
        demonstrates how to modify the replica ring.

        The following screen apprears: 

        NetWare 4.01 Directory Services Repair Utility 

        You selected replica: OU=DETROIT 
        Press "1" to set this server as MASTER in the replica
        ring. 

        Press "2" to manually edit the replica ring. 

        Enter selection, or "0" to quit: 2 

     6. Select option 2 to manually edit the replica ring by
        typing 2.

        This following screen appears which displays the current
        servers that are associated with the DETROIT partition
        ring. The server SERV3- is still present. 

        NetWare 4.01 Directory Services Repair Utility 

        Select a server in the ring of partition: OU=DETROIT 

        Number  State    Type         Server 

        1       Present  MASTER       CN=SERV4-
        2       Deleted  SUBORDINATE  CN=WARLOCKS
        3       Present  SUBORDINATE  CN=SERV3-
        4       Present  SUBORDINATE  CN=SERV2- 
        5       Present  SUBORDINATE  CN=SERV1-

        Enter the number of the server to delete, or "0" to
        quit: 3 

    7.  Select SERV3- (number 3) from the ring by typing 3.

        This deletes the server from the replica ring and the
        following screen appears:

        NetWare 4.01 Directory Services Repair Utility 

        Select a server in the ring of partition: OU=DETROIT 

        Number  State    Type         Server 

        1       Present  MASTER       CN=SERV4-
        2       Deleted  SUBORDINATE  CN=WARLOCKS
        3       Deleted  SUBORDINATE  CN=SERV3-
        4       Present  SUBORDINATE  CN=SERV2- 
        5       Present  SUBORDINATE  CN=SERV1-

        Enter the number of the server to delete, or "0" to
        quit: 0 

     8. Exit the replica ring editor by typing "0" (zero). 

================================================================
Disclaimer     

Novell, Inc. makes no representations or warranties with respect
to the contents or use of this document, and specifically
disclaims any express or implied warranties of merchantability
or fitness for any particular purpose. Further, Novell, Inc.
reserves the right to revise this publication and to make 
changes to its content, at any time, without obligation to
notify any person or entity of such revisions or changes.

Novell, Inc., makes no representations or warranties with
respect to any NetWare software, and specifically disclaims any
express or implied warranties of merchantability, title, or
fitness for a particular purpose.  Distribution of any 
NetWare software is forbidden without the express written
consent of Novell, Inc.

Further, Novell reserves the right to discontinue distribution
of any NetWare software. 

Novell is not responsible for lost profits or revenue, loss of
use of the software, loss of data, costs of recreating lost
data, the cost of any substitute equipment or program, or claims
by any party other than you.

Novell strongly recommends a backup be made before any software
is installed. Technical support for this software may be
provided at the discretion of Novell.

Trademarks

Novell, Inc. has attempted to supply trademark information about
company names, products, and services mentioned in this
document.

The following list of trademarks was derived from various
sources.

Novell and NetWare are registered trademarks NetWare 4.01,
NetWare 4.02, NetWare 4,NetWare Client, NetWare Directory
Services and NDS, and NLM are trademarks of Novell, Inc.

All other products and company names are trademarks or
registered trademarks of their respective holders.