Earth Monitor
                                                                   
                         Earthquake Monitoring and Display Software
                                      for the IBM Personal Computer
                                                                   
                                 Document created with version 5.17
                          Current version is 6.1 (as of 1 May 1995)
                                                                   



                                                      June 26, 1995


                                                          Ted Blank

                                                           Address:
                                                  954 Foxswallow Ct
                                     San Jose, California USA 95120
                                                     (408) 323-8514
                                                                   
                                             Compuserve: 71651,1416
                                      Internet:   tblank@netcom.com
                              FTP: /pub/tb/tblank at ftp.netcom.com








CONTENTS


  Introduction   . . . . . . . . . . . . . . . . . . . . . . . . . . 1
    Where to find a seismometer  . . . . . . . . . . . . . . . . . . 1
  The EMON Software Package  . . . . . . . . . . . . . . . . . . . . 1
    What kind of PC should I use?    . . . . . . . . . . . . . . . . 1
  Package Contents   . . . . . . . . . . . . . . . . . . . . . . . . 2
  Monitoring Seismic Activity with EMON  . . . . . . . . . . . . . . 3
    Customizing EMON: the OPT file   . . . . . . . . . . . . . . . . 4
  Displaying earthquake recordings with QUAKEVU  . . . . . . . . . . 4
    QUAKEVU V6 special note  . . . . . . . . . . . . . . . . . . . . 7
    Customizing QUAKEVU startup: the INI file  . . . . . . . . . . . 7
  Utility programs   . . . . . . . . . . . . . . . . . . . . . . . . 8
    EL (EMONList)  . . . . . . . . . . . . . . . . . . . . . . . . . 8
    HOWFAR   . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8
    MSPLICE  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9

  Hardware  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 11
  PC Clock  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 11
  Analog-to-Digital Converter (ADC) Card  . . . . . . . . . . . . . 11
    Addressing  . . . . . . . . . . . . . . . . . . . . . . . . . . 12
  Signal Amplifier and Filter   . . . . . . . . . . . . . . . . . . 14
    Amplification level ("gain")  . . . . . . . . . . . . . . . . . 14

  Software description  . . . . . . . . . . . . . . . . . . . . . . 15
  Data collection   . . . . . . . . . . . . . . . . . . . . . . . . 15
    Trigger Algorithm   . . . . . . . . . . . . . . . . . . . . . . 15
    EMON Options File   . . . . . . . . . . . . . . . . . . . . . . 16
      Parameters which are new in Version 6.1   . . . . . . . . . . 21
      Parameters which are new in Version 6.0a-k  . . . . . . . . . 21
      Parameters which existed in Version 5.xx  . . . . . . . . . . 24
    EMON Main Screen  . . . . . . . . . . . . . . . . . . . . . . . 29
      Header area   . . . . . . . . . . . . . . . . . . . . . . . . 30
      Seismometer output display area   . . . . . . . . . . . . . . 30
      Filename display area   . . . . . . . . . . . . . . . . . . . 30
    EMON Keyboard Actions   . . . . . . . . . . . . . . . . . . . . 31
    ADC boards supported  . . . . . . . . . . . . . . . . . . . . . 32
  Displaying quake files with QUAKEVU   . . . . . . . . . . . . . . 32
    QUAKEVU features  . . . . . . . . . . . . . . . . . . . . . . . 33
    Mouse Interface to QUAKEVU  . . . . . . . . . . . . . . . . . . 33
    Arrow keys while Zoom'ed  . . . . . . . . . . . . . . . . . . . 33
    Printing the screen from QUAKEVU  . . . . . . . . . . . . . . . 34
    QUAKEVU example   . . . . . . . . . . . . . . . . . . . . . . . 34
    Saving a subset of the original file  . . . . . . . . . . . . . 39
    Printing the screen contents  . . . . . . . . . . . . . . . . . 39
  Data files  . . . . . . . . . . . . . . . . . . . . . . . . . . . 39
    Data File Names   . . . . . . . . . . . . . . . . . . . . . . . 40
      Data file names for files created by EMON V5  . . . . . . . . 40
      Data file names for files created by EMON V6  . . . . . . . . 40

  Bibliography  . . . . . . . . . . . . . . . . . . . . . . . . . . 41
  General Background  . . . . . . . . . . . . . . . . . . . . . . . 41
  Seismic Monitoring Station Practices  . . . . . . . . . . . . . . 41
  Home Seismometer Construction and Design  . . . . . . . . . . . . 41


                                                          Contents  ii






  Earthquake Interpretation   . . . . . . . . . . . . . . . . . . . 41
  Personal Computer Data Acquisition  . . . . . . . . . . . . . . . 42
  Seismic Software Design   . . . . . . . . . . . . . . . . . . . . 42
  Seismometers in the Classroom   . . . . . . . . . . . . . . . . . 42





















































                                                         Contents  iii






FIGURES

  Figure 1. EMON display   . . . . . . . . . . . . . . . . . . . . . 4
  Figure 2. Sample QUAKEVU screen  . . . . . . . . . . . . . . . . . 4
  Figure 3. NEIC earthquake location information.    . . . . . . . . 7
  Figure 4. Contents of HOWFAR.LOC file  . . . . . . . . . . . . . . 9
  Figure 5. Combining parts of two files into one file with MSPLICE  10
  Figure 6. OPT file for single-address, single-channel ADC   . . . 13
  Figure 7. OPT file for single-address, multi-channel ADC  . . . . 13
  Figure 8. Noise detection in trigger algorithm  . . . . . . . . . 15
  Figure 9. EMON typical screen display   . . . . . . . . . . . . . 30
  Figure 10. Initial QUAKEVU display using QuickDisplay (/Q) option  36
  Figure 11. Zoom display of the area of interest.    . . . . . . . 37
  Figure 12. QUAKEVU screen after turning QuickDisplay off  . . . . 38
  Figure 13. Origin time & distance calc. using P/S pointers  . . . 39










































                                                           Figures  iv






INTRODUCTION

The personal computer  has been used productively in laboratories as a
data collection device for many  years.  Now,  amateur scientists  can
also  take  advantage of the power of the  personal computer.  If  you
have  a  PC and an interest  in the Earth sciences, you might  want to
consider  setting  up a seismic monitoring station at  home  or  in  a
classroom.  Excellent  results  can  be   obtained  with  a  home-made
seismometer,  constructed  from readily available  materials.  Several
Scientific  American  articles  over  the  past  15   years  (see  the
bibliography)   give  instructions  for   building  various  types  of
seismometers.   Mercury  tilt-meters,  pendulum-based   designs,   and
capacitance-based designs are  just some of  the approaches that  have
been tried with excellent results.

All of the early amateur seismograph designs  used  some sort of chart
recorder to make a permanent record of an amplified earthquake signal.
With the EMON software package, your  PC can do  the  job of the chart
recorder- and much more!  Saving earthquake records to disk allows the
power of the  PC to be applied to the  data analysis - a task at which
the computer excels.


WHERE TO FIND A SEISMOMETER

While you might salvage a seismometer from a local college or research
laboratory, don't dismiss the homemade idea prematurely.  Building one
can be lots of fun and makes an excellent  home or  classroom project.
It  is decidedly low-tech in  nature,  and inspires rich possibilities
for further exploration.


THE EMON SOFTWARE PACKAGE

The collection of programs in this package will let you

þ  view the signal from your seismometer in real time,

þ  save earthquake recordings to disk,

þ  display and analyze the earthquake records, and

þ  zoom in on interesting parts of the earthquake records.

It  is  the  PC  of  course  that  makes the last  three  capabilities
possible.


WHAT KIND OF PC SHOULD I USE?

The same PC can be used for both data collection  and analysis, or you
can use two different  PCs.  The PC  you use for data collection  does
not need to be particularly powerful.  In fact, an old  IBM PC/XT (the
first PC to have a hard  drive) with an  internal  or  external 3 1/2"
floppy drive  installed  is  just  about the  perfect data  collection


                                                       Introduction  1






machine.  The  hard drive allows lots of data to be collected, and the
floppy drive  allows you to archive  the important files or share them
with friends.

When it is  time  to display  and  analyze the  data  though, a faster
machine (minimum of 286 class,  but the faster  the better) makes this
part much  more  enjoyable.  If you  want to display your  data  on  a
different PC than the one on which it was  collected, just  make  sure
the  two machines have at least one  size of floppy disk in common, or
some sort  of  serial or parallel  port  connection  which allows file
transfer.

Also,  remember to keep good  written records.  From the day you start
monitoring for earthquakes, keep a log  or  journal.  Anytime you make
any change to your  system, write down  what you've done in  your log.
This way others will know what has changed.

You might want to start a folder for  each significant  earthquake you
record.  Keep  a printout of the record in the folder,  along  with  a
disk containing a copy of the quake file.  You might  also want to put
a  map  on  the wall  of your station  with a pin  in  the location of
earthquake you've recorded.


PACKAGE CONTENTS

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  Table 1. EMON package contents.  This table describes the contents³                                                                    ³
           of the EMON package.³                                                                    ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  Filename       Description                                        ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  EMON.EXE       Monitors, displays and records output of the       ³              ³                                                     ³
                 seismometer                                        ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  EMON6.OPT      Options file you use to customize EMON for your    ³              ³                                                     ³
                 location.  First time users of EMON should rename  ³              ³                                                     ³
                 this file as EMON.OPT and then customize.          ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  EMON6NEW.OPT   File containing only options new to Version 6 of   ³              ³                                                     ³
                 EMON.  Current users of EMON should add the        ³              ³                                                     ³
                 contents of this file to their existing EMON.OPT   ³              ³                                                     ³
                 file, and then customize the new options.          ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  EMON61NW.OPT   File containing only options new to Version 6.1 of ³              ³                                                     ³
                 EMON.  Current users of Version 6 of EMON should   ³              ³                                                     ³
                 add the contents of this file to their existing    ³              ³                                                     ³
                 EMON.OPT file, and then customize the new options. ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  QUAKEVU.EXE    Displays and lets you analyze quake files          ³              ³                                                     ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ






                                                       Introduction  2






ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Table 1 (Page 2). EMON package contents.                           ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  Filename       Description                                        ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  QUAKEVU.INI    File which tells QUAKEVU in which mode to start.   ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  EL.EXE         Displays full screen list of quake files on disk.  ³              ³                                                     ³
                 From this screen you can display files with        ³              ³                                                     ³
                 QUAKEVU.                                           ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  MSPLICE.EXE    Splices together two or more consecutive quake     ³              ³                                                     ³
                 files into one file.  A full screen list of files  ³              ³                                                     ³
                 is presented.  You may select any number for       ³              ³                                                     ³
                 splicing.                                          ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  HOWFAR.EXE     Calculates the great circle distance between two   ³              ³                                                     ³
                 points on the earth's surface given their latitude ³              ³                                                     ³
                 and longitude.                                     ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  EMON.DOC       This file.  Print via COPY EMON.DOC LPT1: command. ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  READ.ME        Instructions for printing documentation, etc.      ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  HOWFAR.LOC     Sample of a file containing the name, latitude and ³              ³                                                     ³
                 longitude of your station, for use by the HOWFAR   ³              ³                                                     ³
                 program.  Optional.                                ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  93019OIN.TBJ   Quake file from a magnitude 6.0 earthquake of Jan  ³              ³                                                     ³
                 19, 1993 at 14:39:27.4 UTC off the island of       ³              ³                                                     ³
                 Hokkaido in the Sea of Japan.  This was an         ³              ³                                                     ³
                 aftershock of the 6.9 quake of January 15 which was³              ³                                                     ³
                 the largest the area had experienced in 11 years.  ³              ³                                                     ³
                 The recording was made in downtown Tokyo.          ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  ALASKA.DAT     Quake file from a magnitude 6.6 earthquake in      ³              ³                                                     ³
                 Alaska. The recording was made in New York State.  ³              ³                                                     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  NEWHAMP.DAT    Quake file from a smaller earthquake in Berlin, New³              ³                                                     ³
                 Hampshire.  This recording was also made in New    ³              ³                                                     ³
                 York State.                                        ³              ³                                                     ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ



MONITORING SEISMIC ACTIVITY WITH EMON

The Earth Monitor (EMON) program is designed to run continuously in
the PC.  It  periodically checks the input from the seismometer and
amplifier for earthquake-like activity.  An earthquake data file is
saved  to disk only  when an  earthquake  signal  is  detected.  An
options file called  EMON.OPT is  read at startup.  You  can change
the parameters that control saving data  by changing entries in the
OPT  file.  You  can collect data  from  up  to  three seismometers
simultaneously.  A separate  quake file  will  be  written for each


                                                       Introduction  3






device.

Figure 1 shows a sample of  how the EMON  screen appears when it is
monitoring for  earthquakes.  Notice  that  three  quake files have
already been  saved to disk, and their names appear in the space at
the  bottom of  the screen.  If your PC has graphics capability (as
this one  did), the box  at  the  upper right displays  a real-time
trace of the output of the seismometer.  However,  EMON can collect
data on  a  PC which does not  have graphics capability.  You  will
just  need to use a different PC to  display the data later.  "EMON
Main Screen" on page 29  goes into more detail on using EMON.

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Figure 1. EMON display



CUSTOMIZING EMON: THE OPT FILE

Earthquake recording stations differ in more than just their location.
For instance,  a  quiet location in  the  country  could record small,
distant  events without worrying about interference from local  noise,
whereas a location in  a  large  city  might need  to  more  carefully
discriminate earthquake activity from  earth movements due to  trains,
subways or the like.

You customize EMON for the characteristics of your location through an
options  file called  EMON.OPT.  You can edit this file with any ascii
text editor.  Do not use word processors!  The  EMON.OPT file  is read
from disk when the program starts.  It should be in the same directory
as the EMON program.  In  the  OPT file you give EMON information like
the local noise level (used to discriminate true seismic activity from
local  noise).  Other  information  you  supply  includes  the   three
character ID of your station (which becomes  the file extension on all
saved files) and the disk (or  directory)  to which you want the quake
files to be saved.  You can also change some  of these same parameters
on  the screen after EMON has  started.  However, changing a parameter
on the  screen does notmake the  change  permanent.  You must edit the
EMON  file  and make the same change if  you  wish it  to be effective
automatically every time the EMON program starts.  "EMON Options File"
on page 16 explains each parameter in the options file.


DISPLAYING EARTHQUAKE RECORDINGS WITH QUAKEVU

The QUAKEVU program displays the data files created by EMON.  Figure 2
shows a sample of the QUAKEVU screen.

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Figure 2. Sample QUAKEVU screen

QUAKEVU allows you to identify the P and S wave arrivals on the screen
by moving small pointers via either  the mouse  or  the keyboard arrow


                                                       Introduction  4






keys.  Once  you  have  picked out  the P  and S  wave arrival points,
QUAKEVU then automatically calculates for you

þ  the time the P wave arrived at the recording station

þ  the time the S wave arrived at the recording station

þ  the time the quake occurred (the Origin time)

þ  the  distance from the recording  station  to the epicenter of  the
   quake along a great-circle arc (in kilometers, miles and degrees)

This information is updated  every time  you move  either the P  or  S
pointers.

Notice that QUAKEVU  does not calculate the locationof the earthquake,
just the distance from the recording station.  You will need to obtain
distance calculations from at least three stations  in different parts
of  the  globe, and use triangulation on a map  or globe to figure out
the actual  location.  This  makes  it fun  to trade  quake files with
other groups who also monitor earthquakes.

QUAKEVU will also allow you to save  a subset of the data to a smaller
file  for  easier  transmission  across telephone  lines.  During  the
process  of  saving the subset file you  can also add a comment to the
file being saved (up to 60  characters)  as  well  as the true  origin
time, depth, location etc. if you know them.

QUAKEVU will work only on a PC with a Color Graphics Adapter (CGA) and
graphics  display,  or  its   equivalent.  QUAKEVU  uses  the  CGA  in
"hi-resolution" (640x200) mode,  which is equivalent  to "SCREEN 2" in
BASIC.  (In  this  mode  only  black  and white are  available.)  Most
computers with any type of  graphics  capability support this graphics
mode, since it has been around almost since the PC was invented.

You can display from one to three recordings of the same earthquake on
the screen at the same time.

Note: An OS/2  and  Windows  version of  QUAKEVU  called  WinQuake  is
available  from  Larry  Cochrane,  24   Garden   St.,  Redwood   City,
California.  This package  is a major  improvement on  QUAKEVU  in all
respects but  does require  Windows  (either DOS/Windows  or  the OS/2
Windows) and a 386 or 486 CPU.  It is available via anonymous FTP from
the /pub/cochrane directory of the ftp.netcom.com Internet system.

Each earthquake data file  contains  reserved space for a 60 character
comment describing the contents  of  the file.  QUAKEVU will allow you
to  to insert text into this reserved area when you save a file.  Once
a comment area is  filled  in, QUAKEVU displays it on the screen  when
the   file   is   displayed.   This   allows   a   limited   form   of
self-documentation for  the data files.  For  instance, you might want
to add a comment like "ML6.6 Solomon Islands  11S 163.5E".  This would
remind when you  displayed  the  quake file of the  magnitude  (on the
Richter scale), the  location, and the latitude and longitude  of  the
quake being displayed.  Note that the recording station name (up to 15


                                                       Introduction  5






characters) is already  saved in the file  in  a  different  place, so
there is no need to add that to the comment.

You can get information on the true  location of  the  earthquake from
news  reports  or, if  your PC has  a modem,  via  a call to the  U.S.
National Earthquake Information Center (NEIC) computer bulletin board.
Within a few  hours of a  major  quake, the NEIC  in Golden, Colorado,
makes a preliminary determination of its location using data just like
you  will  be  collecting  from  stations  all  around the world  that
recorded the event.  An  example of one of  their messages is given in
Figure 3  on  page 7.  It  is  sent out as  soon as possible to assist
disaster relief  agencies around the world  in  responding quickly  to
major earthquakes.  Location of smaller quakes are  usually calculated
and available within 1-2 weeks after the event.











































                                                       Introduction  6






ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
    U.S. GEOLOGICAL SURVEY  NATIONAL EARTHQUAKE INFORMATION CENTER
                    World Data Center A for Seismology

the following is from the united states geological survey,  national
earthquake   information   center:    preliminary   hypocenter   for
earthquake of 1993 jan 19, SEA  OF  JAPAN:   latitude  38.7  degrees
north  longitude 133.5 degrees east origin time 14 39 27.4 utc depth
460, magnitude 6.0 mb.
stations used:  mat p 144044.0 smy p 144507.9 adk p 144552.9
sdn p 144707.8 brw p 144719.7 tta p 144721.5 svw p 144724.9
ima p 144727.3 ap 144845.3 bgl p 144736.2 crp p 144736.5
ap 144907.5 cp2 p 144736.8 kdc p 144738.8 ap 144850.9
.
.
.
tuc p 145126.6 alq p 145130.1 ap 145312.8 wmok p 145148.8
tbr p 145208.0 nav p 145214.4 bla p 145216.3 cvl p 145216.7
ceh p 145223.6 prm p 145225.3 jsc p 145226.7 lhs p 145226.9
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Figure 3. NEIC earthquake location information.



QUAKEVU V6 SPECIAL NOTE

In version 6  and higher  versions of EMON, additional space is placed
in the data file describing  the sensor  that was used to  record  the
quake.  Additional  space is reserved in the file  into  which you can
add

þ  Magnitude

þ  Method by which magnitude was computed (4 chars)

þ  Depth (in km)

þ  Latitude and longitude



CUSTOMIZING QUAKEVU STARTUP: THE INI FILE

Different users found they used QUAKEVU in different ways.  Some  with
slower  PCs  start in QuickDisplay mode, zoom  in on a portion of  the
file,   then  display  at  full   resolution.  Others  like  to  start
immediately identifying  the P  and  S  waves  to get an  estimate  of
distance.

Since there was no way to  satisfy  all these  different requirements,
QUAKEVU V6 now includes a  file called QUAKEVU.INI which tells QUAKEVU
how to start  up.  After  starting the program you can continue to use
the keyboard or mouse as  before.  You  can edit the INI file with any
ASCII text editor.  Don't use word processors!



                                                       Introduction  7






UTILITY PROGRAMS

Several utility programs are included to  assist in handling the files
after they are collected.


EL (EMONLIST)

EL.EXE is the EMONList program.  EL  ?  gets you help.  Just  supply a
filemask  in standard form,  like *.*  or  93*.*  and EL will find all
matching  files  in  the  current  directory  (or  the  directory  you
specify).  It  lists the peak sample, date and  time sampling started,
and the first  40  characters or so of the  comment.  Hit enter on any
line to view that file with QUAKEVU.  You  can  also  use the UpArrow,
DownArrow,  PgUp, PgDn,  Home  and End  keys to  move around the list.
Pressing the Del key will erase the file from disk (after giving you a
chance to confirm).  Deleting a file will remove it from the on-screen
list as well.

If you have several files for the same quake from different locations,
you can view all of them on the same QUAKEVU screen.  To do this, mark
up to three files with the spacebar.  An  "X"  will appear in front of
the name of the file.  When all files have been marked,  press enter -
QUAKEVU  will  then  load all three  and  display  them  on  the  same
timescale.


HOWFAR

The HOWFAR program computes the great circle  distance between any two
points  on  the  earth given  the latitude and longitude of each.  You
will be prompted for both sets of coordinates.  However, if you create
a file called HOWFAR.LOC containing the latitude and longitude of your
station,  the HOWFAR program will use that information as  one of  the
locations and you only need to enter the second  one.  The  HOWFAR.LOC
file must be in the same directory as HOWFAR.EXE.  The  format of  the
HOWFAR.LOC file is:




















                                                       Introduction  8






ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
LINE 1 - Text describing the place that this set of coordinates
         refers to.  For instance, you might put something like:
            XYZ School, Woonsocket, RI

LINE 2 - latitude in degrees, e.g. 43.52.  Use negative numbers
         if you are SOUTH of the equator.

LINE 3 - longitude in degrees, e.g. 108.16.  Use negative numbers
         if you are in the half of the world WEST of Greenwich.

Example for Tokyo, Japan station at 35.65 N latitude and 139.72 E longitude:

Tokyo, Japan
35.65
139.72

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Figure 4. Contents of HOWFAR.LOC file



MSPLICE

The recent 7.8 quake in Bolivia released an enormous amount of energy.
At one user's  station,  6  EMON files were saved from this one  great
quake.  Rather  than dealing with  these  files one  at  a  time,  the
MSPLICE program allows you to splice together two  or more  data files
which, back-to-back, span a long event.

Figure 5 on page 10 shows  this procedure.  The earthquake starts late
in the first file and continues into the second file.  MSPLICE subsets
the samples in both files until the total  is  less  than  or equal to
25000.  (EMON  data files can only contain up to 25000 samples.)  Then
both sets of data are are combined into a new file spanning the entire
event, although at a lower resolution.





















                                                       Introduction  9






ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Original files
(25000 samples  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ******###       #########*******ÄÄÄÄÄÄÄÄ
 each)
                                  ³                  ³
                                  ³                  ³
                                  v                  v

Subset files
(Every other     Ä Ä Ä Ä Ä Ä Ä * * * # #       # # # # # * * * Ä Ä Ä Ä
 sample
 discarded)                       ³                  ³
                                  ÀÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÙ
                                           ³
                                           ³
                                           v

Combined file
 (25000 samples)               Ä******############*******Ä

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Figure 5. Combining parts of two files into one file with MSPLICE


































                                                      Introduction  10






HARDWARE

Up to now  we've  talked  only  about the  software side of running  a
seismic monitoring station.  However  it  is  important  to  have some
familiarity  with  the hardware  required to interface  a  PC  to  the
"outside world".  The three pieces of hardware we will discuss are the
PC clock, the  analog-to-digital  converter (ADC) card, and the signal
amplifier.


PC CLOCK

An  accurate  PC  clock  is  a  must  for  seismic   data  collection.
Scientists  have  agreed   that   all  monitoring  stations  will  use
Coordinated Universal  Time (UTC,  formerly  known as  Greenwich  Mean
Time).  You should therefore keep your PC set  to UTC time rather than
local time.  In the U.S.A., a call to 1-900-410-TIME  will cost you 50
cents and  will allow you  to  set your  PC  clock to  the  U.S. Naval
Observatory Master Clock.  If you have a short-wave radio, the British
Broadcasting Company  (BBC) accurately  marks the  time  on  the hour.
Also, several packages are on the market  to  continuously synchronize
your PC clock to the WWV time  signal which can be received in most of
the  continental US.  Beware of daylight savings time - it may  affect
the number of hours between your time and UTC.

If you find that  your  PC clock does not maintain  the  correct time,
there may be  add-in clock boards available which keep excellent time.
The factory clocks  in some older PCs may drift as  much as a minute a
week.  You should try to keep  your PC within one second  of true UTC.
Shareware programs like RighTime and AccuSet, available on  Compuserve
and  other  bulletin board systems,  can  also  help  your PC stay "on
time".


ANALOG-TO-DIGITAL CONVERTER (ADC) CARD

The job of an ADC card is to convert an analog signal from the outside
world,  usually a voltage, into a digital  signal - a range of numbers
that  a  computer  can  manipulate.  (This  process  is also  known as
"digitizing").  Low voltage = small number, high voltage = big number.
(Sometimes the range is from a negative number to  the  same  positive
number.)  Each card has  a different  "smallest" and "biggest" number.
Here, as in most places, you get what you pay for.  An inexpensive ADC
card might  convert a range of input voltages (say, 0 to 5 volts) into
numbers from zero to 255.  Zero would represent the lowest voltage and
255 would represent the highest voltage.

A more sensitive  (and expensive) ADC card might be able to divide the
same  5-volt range into many  more than  just 255 separate steps.  For
seismographic work  you  should  choose  only  an  ADC card which  can
convert a  voltage range  into a  range of  at  least  4096  different
numbers.  A card with this capability is called a "12-bit" card, since
it's  output has 12 "bits" (binary digits)  of data, which  gives 4096
possible combinations  of ones and zeros.  "13-bit" and "14-bit" cards
are also available, but will probably only be worth the extra money in


                                                          Hardware  11






very quiet locations.

The  ADC card  usually fits into  an  expansion  slot  on the PC  main
circuit board.  Since there  may be several cards installed, all cards
are  designed  to  have  different  addresses and  to respond  only to
commands  directed to that address.  The EMON program uses this scheme
to send commands to the ADC card.  So how do you tell EMON the address
of your ADC card?


ADDRESSING

Each add-on card in  a  PC  is  designed to  respond to  commands to a
specific address.  However, different  manufacturers don't always know
which addresses other manufacturers are using.  Most companies now put
switches  on their cards so that  the  user (that's you!)  can  choose
another address for  the  card  if the  address set  at the factory is
already in use by another card in your  PC.  You  will need the manual
supplied with  the  ADC card to change the switches from their factory
setting.  However, most of the time you can use the address set at the
factory.  You will find this in  the documentation that  came with the
card.

ADC card designers are very creative.  There  are many different types
of  ADC  cards  on  the market  with  many  different  features.  EMON
currently supports 9 different types of cards which are  listed in the
EMON.OPT file.  For  amateur purposes I group them  into the following
categories:

    Single-address, single-channel

    Single-address, multi-channel

    Multi-address, multi-channel

Each section  below includes  an  example of how  you might set up the
EMON.OPT file for that type of card.  Each example assumes you want to
monitor more than one seismometer.  If you have only one, just set the
second and third seismometer addresses to zero  and EMON  will  ignore
them.  In EMON version 6.1 and higher, use  the FirstSeismometerActive
(etc.) options in the EMON.OPT file to control  how many channels EMON
will sample from.  Starting in v6.1, only these parameters and not the
zero  address  controls the  devices  which  are  monitored.  This  is
because  some  cards can use three zero addresses and only change  the
channel being sampled.

þ  Single-address, single-channel

   Only the very  cheapest and  simplest cards are of this  type.  One
   card can monitor only one  device.  Each  seismometer you wished to
   monitor would therefore require a separate card  and thus an entire
   expansion slot.

   Here is an  example  of  part of the OPT file for a single-address,
   single-channel card.


                                                          Hardware  12






ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

FirstSeismometerActive =     Yes      'Active and being sampled (EMON v6.1+)
FirstSeismometerOrientation =  N      'Orientation (N = North/South)
FirstSeismometerAddress =    340      'Decimal Address of 1st seismometer
FirstSeismometerChannel =      0      'Channel for 1st seismometer

SecondSeismometerActive =    Yes      'Active and being sampled
SecondSeismometerOrientation = E      'Orientation (E = East/West)
SecondSeismometerAddress =   341      'Decimal Address (0 if not installed)
SecondSeismometerChannel =     0      'Channel for 2nd seismometer

ThirdSeismometerActive =     Yes      'Active and being sampled
ThirdSeismometerOrientation =  Z      'Orientation (Z = Vertical)
ThirdSeismometerAddress =    342      'Decimal Address (0 if not installed)
ThirdSeismometerChannel =      0      'Channel for 3rd seismometer
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Figure 6. OPT file for single-address, single-channel ADC

þ  Single-address, multi-channel

   This is  the most common type  of  card.  Several  different  input
   channels (signals)  can be  monitored by  this  type  of card while
   taking up only one expansion slot.

   The OPT file for this type of card might look like this:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

FirstSeismometerActive =     Yes      'Active and being sampled
FirstSeismometerOrientation =  N      'Orientation (N = North/South)
FirstSeismometerAddress =    340      'Decimal Address of 1st seismometer
FirstSeismometerChannel =      0      'Channel for 1st seismometer

SecondSeismometerActive =    Yes      'Active and being sampled
SecondSeismometerOrientation = E      'Orientation (E = East/West)
SecondSeismometerAddress =   340      'Decimal Address of 2nd seismometer
SecondSeismometerChannel =     1      'Channel for 2nd seismometer

ThirdSeismometerActive =     Yes      'Active and being sampled
ThirdSeismometerOrientation =  Z      'Orientation (Z = Vertical)
ThirdSeismometerAddress =    340      'Decimal Address of third seismometer
ThirdSeismometerChannel =      2      'Channel for 3rd seismometer
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Figure 7. OPT file for single-address, multi-channel ADC

þ  Multi-address, multi-channel

   In this type of ADC, the same card responds to commands directed to
   any of several  different  addresses.  One card can monitor several
   different channels, with each address corresponding  to a different


                                                          Hardware  13






   channel.  The  "base  address"  of  the  card  monitors  the  first
   channel,  the  "base address plus 1" reads the second channel, etc.
   The  OPT  file  entries  would  be  identical  to   those  for  the
   "single-address,  single  channel" card  described above.  However,
   commands to any of the three addresses would  actually be processed
   by  the same card  instead  of being  processed by  three different
   cards.



SIGNAL AMPLIFIER AND FILTER

ADC cards usually are able to  senser  voltages as  low as 1 millivolt
(1/1000  volt).  However,   the  voltage  output  from  a  seismometer
responding to the passage  of  an earthquake wave from a distant event
might be  only 1 microvolt (1/1,000,000 V).  In  this  case  no signal
would be recorded.

For this  reason  the voltage output of  the  seismometer  is  usually
amplified  by  a factor  of from several  hundred to several  thousand
before it is sent to the ADC card.  In addition, noise from electrical
equipment is usually filtered out before the signal is amplified.


AMPLIFICATION LEVEL ("GAIN")

If you use a  higher amplification level (also called "gain") you will
be able to record more distant large events, and smaller local events.
However if  your local environment  is noisy, turning up the gain will
amplify local noise as well.  This noise will usually be of two types:
60 cycle noise  from home electrical devices, and  low-frequency noise
from  traffic,   wind,  home  appliances  and  (of  course)  children.
Electronic  filters can  remove  most 60 cycle noise.  However,  lower
frequency  noise can  be difficult  to  distinguish  from the  seismic
signals themselves.  A general rule  then is to turn the amplification
level on your amplifier up until  you begin to see  too much noise  in
the  signal (too  much vertical jitter)  or begin  recording  too many
"false alarms", and then turn it back down a bit.  Now experiment with
the      EMON.OPT       parameters      "NoiseRangeToIgnore"       and
"SampleCountToSaveFile" to minimize the number of false alarms.

Now let's take a more detailed look at the programs.















                                                          Hardware  14






SOFTWARE DESCRIPTION



DATA COLLECTION

The EMON program performs the monitoring and collection of the seismic
data.  The  program  saves  data to disk only when it  appears that  a
quake  has been  detected.  For this  purpose it  includes  a  trigger
algorithm - a kind of decision-making process which you can control.


TRIGGER ALGORITHM

The  purpose  of a  trigger algorithm is to detect earthquake activity
while screening  out false  alarms.  The  algorithm  I chose uses  the
concept of a "noise  zone"  around the normal output value  of the A/D
converter.  You specify the  width of this "noise zone" (in percentage
of full range  of  the ADC card) in the "NoiseRangeToIgnore" parameter
in   EMON.OPT.  See  "hdref  refid=opt..  for   descriptions  of   the
parameters in the EMON.OPT  file.  Signals  outside  (above  or below)
this noise  zone  are the important ones.  The  number of samples that
fall above or  below the noise  zone are counted as the program  runs.
Periodically  EMON  checks  to  see  if  at least a certain  number of
samples   (a   number    you    choose    via   the    OPT   parameter
"SampleCountToSaveFile")  has  been observed both above and below this
zone.

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                        o
Upper "Quiet" zone     o o      <- 5 samples above upper boundary
                      o   o
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ-   upper noise zone boundary
N  Z       SIGNAL    o    o
O  O    o   o o   o o                  o o
I  N    ÄoÄoÄÄÄoÄoÄÄÄÄÄÄÄÄÄÄoÄÄÄÄÄÄÄÄÄoÄÄÄoÄ
S  E      o     o            o       o
E                                   o
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ-   lower noise zone boundary
                              o    o
Lower "Quiet" zone             o  o
                                oo     <- 6 samples below lower boundary

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Figure 8. Noise detection in trigger algorithm

If this has  indeed  happened,  the program  assumes a quake event has
occured and begins accumulating data to save to disk.  (A small amount
of  data from before the event started is  also included.)  Otherwise,
the counters are reset to zero and monitoring continues.

If you set  the width of this "noise zone" too narrow, many files with
nothing but noise will be saved to disk  and you will have to  spend a
lot of  time going through them to determine if  they contain anything
of interest.


                                              Software description  15






On the other hand, if you set the "noise zone" too wide, only the very
largest earthquakes will be recorded, and you may only  see one or two
files  per  year!  The  proper  settings  for  the  trigger  algorithm
parameters  are  different  for  every  location,   and  can  only  be
determined by trial and  error.  They may change with the seasons too.
If you  live  near the ocean,  for example, winter storm waves hitting
the shore might generate enough  local seismic noise to force  you  to
temporarily raise the value of "NoiseRangeToIgnore".


EMON OPTIONS FILE

The EMON options file (default name: EMON.OPT) allows you to customize
the  EMON program for your setup  and local seismic  environment.  You
can use any text editor to modify  the file.  Following  is an example
of   an  OPT   file.  The   station  it  is  from  has  the  following
characteristics:

þ  A single IBM  Data  Acquisition  and Control  Adapter card is being
   used to monitor the amplified signals.

þ  Two  seismometers  are being monitored.  The  first (at address 544
   channel  0)  is  in a N-S orientation, the second (at  address  544
   channel 1) is in an E-W orientation.

þ  the local environment is a fairly noisy urban  environment,  making
   it necessary to set  NoiseRangeToIgnore  (or "noise zone")  to 15%.
   In quieter environments, a value as  low as 1 or 2 may be possible.
   Values below 1 are accepted but would  only make sense in extremely
   quiet environments.



























                                              Software description  16






*
* Filename: EMON6.OPT
*
* Sample options file for Earth Monitor (EMON) Seismic Data Acquisition System
*
* If you are a first-time user of EMON, rename this file to EMON.OPT
*                                       ----------------------------
* If you are an existing EMON user you can either:
*
*    1) copy the "New Options" section of this file into your existing
*       EMON.OPT file, or
*
*    2) insert the file EMON6NEW.OPT, which contains only the new options
*       for V6, into your existing EMON.OPT file.
*
* Compatible with version 6.00 and up
* Shipped with version 6.01
* Blank lines or lines beginning with * are comments
* See EMON User's Guide for complete explanations of each parameter.
* Ted Blank, tblank@netcom.com or 71651,1416 on Compuserve

*****************************************************************************
*        New options for EMON Version 6.01                                  *
*****************************************************************************

DisplayTimeCompression =       1      'Compresses display horizontally.
*                                     'Higher numbers display every nth
*                                     'sample, allowing display to run slower
*                                     'than sampling rate.  This leaves data
*                                     'on the screen for a longer time.

FirstSeismometerActive =     Yes      'Specify Yes or No to turn on/off
SecondSeismometerActive =     No      'sampling for each of the three
ThirdSeismometerActive =      No      'possible devices.

*****************************************************************************
*        New options for EMON Version 6.00                                  *
*****************************************************************************

FileNameDisplay =          SHORT      'SHORT: display name only (as in EMON V5)
*                                     'LONG:  display both name and extension

PromptOnQuit =                NO      'YES or NO: safety prompt when quitting?

BeepOnFileSave =              No      'NO     Silent operation.
*                                     'YES    One beep when quake file is saved.
*                                     'ALARM  Beep every 30s until key pressed,
*                                     '       but start when file is saved.
*                                     'IMMEDIATE - Same as ALARM but start
*                                     '       beeping when quake is detected.

AlarmLevel =                  50      'Value from 0 to 99.  Sound alarm only
*                                     'when quake has relative strength at least
*                                     'this large.  NOTE: does not apply if
*                                     'the IMMEDIATE option was selected above.


                                              Software description  17







FileFormat =                 New      'OLD or NEW.  NEW requires QUAKEVU V6.00+
*                                      or WinQuake V1.6+ to view - but these
*                                      new versions of the display programs
*                                      will still work the same with all your
*                                      old data files.  Use OLD only if you
*                                      do not have access to new display pgms.

ActivityLog =                YES      'Mini-trace of EMON activity - start and
*                                      stop times, files saved, etc.

ActivityLogFile =       EMON.LOG      'Log file path, or LPT1: to log to printer
*                                     'NOTE: logging to printer is NOT recom-
*                                     '      mended, since a printer error like
*                                     '      paper-out will stop sampling!

FirstSeismometerMagCorr =       0     'Magnitude correlation factor (WinQuake)
SecondSeismometerMagCorr =      0     'Magnitude correlation - 2nd seismometer
ThirdSeismometerMagCorr =       0     'Magnitude correlation - 3rd seismometer

* FileNamePattern allows you to choose how your data files are named.  Assemble
* the pattern from the building blocks below.  Separate the building blocks with
* either slash /, plus + or dash - characters.  Use the dot . to identify the
* start of the extension.  Note: do not put separator characters around the dot.

FileNamePattern = YY-MM-DD-S-O.III                  'See building blocks below

* ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
* ³            File Name Pattern building blocks to choose from:              ³
* ³                                                                           ³
* ³  YY   = year                            Example:                          ³
* ³  MM   = month                           Quake at 3:03 am on 2 May 94      ³
* ³  DD   = day                             Vertical sensor, 1st quake of day ³
* ³  JJJ  = Julian date (001-366)                                             ³
* ³  HH   = hour (00-23)                    Pattern ----------> File name     ³
* ³  H    = hour (A-X)                      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    ÄÄÄÄÄÄÄÄÄÄÄ-  ³
* ³  TT   = minute (00-59)                  MM-DD-YY-O-S.III    050294Z1.TBJ  ³
* ³  T    = two minute interval (A-Z,0-3)   (QK)+YY+MM+DD.II+S  QK940502.GC1  ³
* ³  O    = Orientation (N, E or Z)         YY/MM/DD/O/S.III    940502Z1.RWC  ³
* ³  S    = seq no. (A-Z,0-9)               YY-MM-DD-II.O-SS    940502RC.N01  ³
* ³  SS   = seq no. (01-99)    "            YY-JJJ-H-M-O.III    9412232Z.MSS  ³
* ³  SSS  = seq no. (001-999)  "                                              ³
* ³  II   = station ID (1st two chars)   * Filename is maximum 8 characters   ³
* ³  III  = station ID (three chars)     * Extension is maximum 3 characters  ³
* ³  (cc) = any character string in ()   * You must use "O" somewhere in the  ³
* ³  .    = . (separates name from ext)     pattern if you have >1 seismometer³
* ³                                                                           ³
* ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

*****************************************************************************
*        Original options from Version 5                                    *
*****************************************************************************
*****************************************************************************
*        Source of input data                                               *
*****************************************************************************


                                              Software description  18







OperatingMode =           Random      ' Normal = data from sensor
*                                     ' Random = data generated randomly
*                                     ' File   = data from pre-existing file
*                                                (name will be prompted for)

*****************************************************************************
*        Describe your hardware (type of A/D card, addresses, etc.)         *
*****************************************************************************

AnalogToDigitalConverterType = 9      'See list below for details

FirstSeismometerOrientation =  E      'Orientation (N = North/South)
FirstSeismometerAddress =    544      'I/O Address of 1st seismometer
FirstSeismometerChannel =      0      'Channel of 1st seismometer

SecondSeismometerOrientation = N      'Orientation (E = East/West)
SecondSeismometerAddress =     0      'I/O Address (0 if not installed)
SecondSeismometerChannel =     1      'Channel (specify 0 if not installed)

ThirdSeismometerOrientation =  Z      'Orientation (Z = Vertical)
ThirdSeismometerAddress =      0      'I/O Address (0 if not installed)
ThirdSeismometerChannel =      2      'Channel (specify 0 if not installed)

SeismometerToMonitor =         E      'Choose one device to monitor (N, E or Z)

AdcValueAtMaxVolts =        4095      'Digital value when signal >= max Volts
AdcValueAtZeroVolts =       2048      'Digital value when signal = 0 Volts
AdcValueAtMinVolts =           0      'Digital value when signal <= min Volts

*****************************************************************************
*        "Trigger" - screens out as many "false alarms" as possible         *
*****************************************************************************

NoiseRangeToIgnore =           5      'Range (%) around ADC zero value to ignore
SampleCountToSaveFile =       25      '# samples outside null zone required
SamplesPerDataPoint =          5      '# samples to average for one data point

*****************************************************************************
*        Describe your station                                              *
*****************************************************************************

*                1---5---10---15
StationName =       San Jose, CA      'Max of 15 characters, single blanks only
StationID =                  FOX      '3 character (A-Z, 0-9) ID for your site
RecordingLatitude =       111.22      'Lat. of station (neg. if S of Equator)
RecordingLongitude =     -333.44      'Long. of station (neg. if W of Greenwich)

*****************************************************************************
*        Customize the look and operation of your station                   *
*****************************************************************************
DisplayLines =                 5      '# lines on screen (0 for no display)
DisplayCompression =          20      'Vertical compression of displayed signal

*                                     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿


                                              Software description  19






SavePath =               C:\QB45      ³Path to use when saving quake files.    ³
*                                     ³Example   Path used                     ³
*                                     ³-------   ------------------------------³
*                                     ³C:        Current directory on C drive  ³
*                                     ³C:\       Root directory on C drive     ³
*                                     ³C:\QUAKES QUAKES directory on C drive   ³
*                                     ³          (first level directory)       ³
*                                     ³QUAKES    QUAKES dir in current PATH    ³
*                                     ³          (might be 1st lvl or sub-dir) ³
*                                     ³\QUAKES   QUAKES dir on current drive   ³
*                                     ³          (first-level directory)       ³
*                                     ³A:        Current directory on A drive  ³
*                                     ³A:\       Root dir on A drive           ³
*                                     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
*
TemporaryBufferSize =       4000      'Size of each temp buffer (max = 8000)
UserCommand1 =         QUAKEVU /      'Commands to execute on marked file ("/"
UserCommand2 =         COPY / A:      'will be replaced by the name of the
*                                     'currently marked file.  Single blanks
*                                     'only please.
ADCOffset =                    0      'Offset to add to each sample if your
*                                      amlifier does not have an "offset" or
*                                      "zero" adjustment.  This value should
*                                      normally be set to zero.
ADCProgrammableGain =         10      'Gain to set when setting the on-board
*                                     'amplifier on some ADC boards like DR110
*                                      (ignored if board in use doesn't support)
*                                      DR110 supports values of: 1, 10 and 100
*****************************************************************************
*        These parameters are no longer used, but are included for          *
*        compatibility with earlier versions of the program, which          *
*        required that they be present.  The are not listed on the          *
*        startup screen.
*****************************************************************************
*
DirectoryProgram =           DIR      'Program to use for listing directories
CopyPath =                    A:      'Path to use when copying files
*
*****************************************************************************
*        The list below shows the A/D devices which are supported by        *
*        EMON.                                                              *
*****************************************************************************
*                                      0 = Burr Brown ADC674A
*                                      1 = IBM Data Acquisition and Control
*                                          Adapter.  Channels 0-3 are
*                                          available for analog input.
*                                          Use Address=0 for the first card
*                                          when using DAC.COM or DACAT.COM.
*                                          (Address 544 is used by special
*                                           versions of the code that write
*                                           directly to the card, bypassing
*                                           DAC.COM).
*                                      2 = Metrabyte DAS-4
*                                      3 = Modified IBM Parallel Printer
*                                          via Jan Froom's COLLECT routine


                                              Software description  20






*                                      4 = A-BUS AN/146
*                                      5 = PC-LAB 714 Super Card.  544 is the
*                                          the default address (hex 220) with
*                                          switches set to 0-0-0-1-0.  For
*                                          this device, the sampled value is
*                                          echoed to D/A channel 1 to drive a
*                                          plotter.  Value of 0 gives -5V,
*                                          value of 16383 gives +5V on D/A.
*                                      6 = MetraByte DAS-16
*                                      7 = PC-LAB 711S
*                                      8 = ACQUTEK PA-CP12
*                                      9 = Real Time Devices DR110 13-bit A/D

The parameters in the OPT file are described in more detail below.


Parameters which are new in Version 6.1

þ  DisplayTimeCompression

   This is a number which controls what portion  of the data collected
   is displayed on the  screen.  A  value  of  1  will  display  every
   sample.  A value of N (where N > 1)  will  display  only  every Nth
   sample.  This will  allow data to remain on  the screen longer, but
   will not affect the sampling rate.

þ  FirstSeismometerActive

þ  SecondSeismometerActive

þ  ThirdSeismometerActive

   -  YES - device will be sampled and data saved.

   -  NO  - device will not be sampled.

   Note: devices must be activated in order, from 1st to 3rd.  Do  not
   skip a device.



Parameters which are new in Version 6.0a-k

þ  FileNameDisplay

   -  SHORT - Display only name of file being saved (not extension).

   -  LONG  - Display  entire name  plus extension of  the file  being
      saved.  To make  room for the  additional  characters,  only the
      hour of the time the file was saved is displayed.

   In the previous version of EMON,  only  the  name of the quake data
   file was displayed on the screen  but not its  extension.  This was
   because the extension was a constant, the location ID.



                                              Software description  21






   In EMON V6 you can now put  variable data  (like a sequence number)
   in the  file extension.  If you choose to put  variable data in the
   file  extension,  you should choose  the LONG option to display the
   entire  file name.  If you choose the LONG option, only the hour of
   the time at which the  file was saved is displayed.  If you  choose
   the SHORT option, both the hour and the minute of the time the file
   was saved are displayed.

þ  PromptOnQuit

   -  YES - Prompt before leaving EMON

   -  NO  - Leave immediately without prompting

   Note: If a  quake is  in  progress,  you  will always  be given the
   opportunity to save the current data before exiting.

þ  BeepOnFileSave

   -  NO  - No beep

   -  YES - Beep when a quake file is saved

   -  ALARM  - Beep every 15 minutes until a  key  is  pressed, once a
      file is saved

   -  IMMEDIATE  -  Same as ALARM but begin beeping immediately when a
      quake is detected, without waiting for a file to be saved.

þ  AlarmLevel

   A  number between 0 and 100.  Each time  a file is saved to disk, a
   "relative strength" value is calculated.  This is  a percentage  of
   the range of the A/D card that the input signal reached during that
   event.  100 means the A/D card reached its limit.  If you only want
   EMON to beep or sound an alarm for larger quakes, set this value to
   a higher number.  If  you  want EMON to beep or sound the alarm for
   all quakes saved to disk, set this value to zero.

   Note: AlarmLevel is activated only if  BeepOnFileSave is set to YES
   or ALARM.  If BeepOnFileSave is set to IMMEDIATE, *all* files  will
   trigger the audible alarm and AlarmLevel will be ignored.

þ  FileFormat

   -  NEW - Generate data files in new version 6.00 format

   -  OLD - Generate data files in old format.

   EMON  V6.00 has the capability  to  write quake data  files  in  an
   improved format.  With the new format files, more information about
   your  ADC card can  be kept in the file,  which  will  allow better
   display  and analysis of the data files.  Also, the new quake  file
   format has room for you to insert more information about  the quake
   (like depth and USGS  magnitude) in new  reserved  locations in the


                                              Software description  22






   file for improved estimates of distance.

   To  display  the new-format data files, you will need QUAKEVU v6.00
   or higher.  If your version of QUAKEVU is older than this, you  can
   tell EMON  to go back to creating old-format  data files by setting
   FileFormat to OLD.  However  it is recommended that you  allow EMON
   to create  the new format files and use QUAKEVU v6.00 or higher, or
   WinQuake v1.6 or higher.  Either of these new display programs will
   still work fine on all your old format data files.

   If you don't specifically set  the FileFormat  parameter,  it  will
   default to NEW.  However, an annoying Note screen will pop up every
   time you start EMON.  To  eliminate this screen, add a line setting
   FileFormat to NEW (or OLD) to your options file.

þ  ActivityLog

   -  YES - Write a record to a trace file for significant events

   -  NO  - No tracing

   The  EMON activity  log  can help you determine what went wrong  if
   there is a problem  saving data files  or figuring out which  files
   correspond to which event.  A one line entry  with date and time is
   appended to the log file each time EMON is started or stopped, or a
   data file is saved to disk.

þ  ActivityLogFile

   If you specifid  YES to ActivityLog, enter the  name of the file to
   use for the EMON activity  log.  The default value is EMON.LOG, and
   the default path is the current drive and directory.

þ  FirstSeismometerMagCorr

þ  SecondSeismometerMagCorr

þ  ThirdSeismometerMagCorr

   The WinQuake  program by Larry Cochrane displays EMON data files in
   a Windows environment.  It has  significant advantages over QUAKEVU
   in usability, and includes some additional function  (like  Fourier
   transforms) as well.  WinQuake  allows  you to define a correlation
   factor  for  your  seismometer which relates the peak  value  in  a
   datafile with  the  magnitude of the quake.  Once  you  empirically
   determine this value you can enter it here and it will be stored in
   all data files saved for that device.  (However, this  is only done
   if you specify FileFormat = NEW).

þ  FileNamePattern

   The FileNamePattern parameter  allows  you  to choose how your data
   files are named.  You  assemble  the  pattern  you  like  best from
   building blocks that  represent items like the  year,  month,  day,
   sequence number, time,  location  ID,  etc.  Separate  the building


                                              Software description  23






   blocks with either  slash /, plus + or dash - characters.  You  can
   also place a  character string  in the file name by enclosing it in
   parentheses.  Use the dot . to identify the start of the extension.
   Note: do not put separator characters around the dot.

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³            File Name Pattern building blocks to choose from:              ³
 ³                                                                           ³
 ³  YY   = year                            Example:                          ³
 ³  MM   = month                           Quake at 3:03 am on 2 May 94      ³
 ³  DD   = day                             Vertical sensor, 1st quake of day ³
 ³  JJJ  = Julian date (001-366)                                             ³
 ³  HH   = hour (00-23)                    Pattern ----------> File name     ³
 ³  H    = hour (A-X)                      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    ÄÄÄÄÄÄÄÄÄÄÄ-  ³
 ³  TT   = minute (00-59)                  MM-DD-YY-O-S.III    050294Z1.TBJ  ³
 ³  T    = two minute interval (A-Z,0-3)   (QK)+YY+MM+DD.II+S  QK940502.GC1  ³
 ³  O    = Orientation (N, E or Z)         YY/MM/DD/O/S.III    940502Z1.RWC  ³
 ³  S    = seq no. (A-Z,0-9)               YY-MM-DD-II.O-SS    940502RC.N01  ³
 ³  SS   = seq no. (01-99)    "            YY-JJJ-H-M-O.III    9412232Z.MSS  ³
 ³  SSS  = seq no. (001-999)  "                                              ³
 ³  II   = station ID (1st two chars)    * Filename is maximum 8 characters  ³
 ³  III  = station ID (three chars)      * Extension is maximum 3 characters ³
 ³  (cc) = character string, any length  * You must use "O" somewhere in the ³
 ³  .    = . (separates name from ext)     pattern if you have >1 seismometer³
 ³                                                                           ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ



Parameters which existed in Version 5.xx

þ  OperatingMode

   EMON can operate (obtain its data) in one of three ways.

   1. Normal

      This is the normal mode of operation in which data  is read from
      the  Analog  to  Digital  Converter  (ADC).  The  card  must  be
      installed and operational or unpredictable results may occur.

   2. Random

      If "random"  is  specified, no  ADC card is necessary to run the
      program.  A random signal will  be generated internally  by  the
      program and displayed on the screen as if it were real data.  In
      "random"  mode the "trigger" algorithm is overridden.  Every set
      of 25000  samples generated is saved on disk as if an earthquake
      had occurred.   You can  use this  mode to test the  program and
      adjust other parameters.

   3. File

      If "file"  is specified, data is read from a previously-recorded
      quake file.  You will be prompted during EMON initialization for


                                              Software description  24






      the  name of  an  existing data file.  This  file will be loaded
      during initialization, and EMON  will  get its input, sample  by
      sample, from  that set  of data.  This capability allows  you to
      test  new trigger settings  on  old  recordings.  When trying  a
      radically new trigger setting, you might want to be sure that an
      event which was seen and saved at the old settings  would not be
      missed at the new settings.

þ  FirstSeismometerOrientation

   Acceptable values are

   -  N for a device whose axis is aligned in a North-South direction,

   -  E  for a device whose axis is aligned in an East-West direction,
      and

   -  Z for a device which is sensitive to vertical motion.

þ  FirstSeismometerAddress

   This  is the decimal I/O address of the  card in the  PC containing
   the   analog-to-digital    converter   chip.   Usually   the   card
   manufacturer provides switches on the card with  which the user can
   choose one of several different addresses.

þ  FirstSeismometerChannel

   Some ADC cards  have  input connectors for  several  inputs.  These
   separate inputs are called channels.  See  "Addressing"  on page 12
   for further information on setting the Address and Channel settings
   for your card.

þ  SecondSeismometerOrientation, Address, Channel

   Same as  for the first seismometer.  Set to 0 if you  do not have a
   second seismometer.

þ  ThirdSeismometerOrientation, Address, Channel

   Same as for the first  seismometer.  Set to 0 if you do not  have a
   third seismometer.

þ  SeismometerToMonitor

   Acceptable  values are N, E or Z.  Choose  which device you wish to
   use for the on-screen real time display.  You can change  this from
   the keyboard while the program is running.

þ  AdcValueAtMaxVolts

þ  AdcValueAtZeroVolts

þ  AdcValueAtMinVolts



                                              Software description  25






   These three parameters tell EMON the range of numbers your ADC card
   generates at (1)  its highest acceptable input voltage, (2) at zero
   volts input, and (3) at its lowest acceptable  input voltage.  Some
   cards  convert  voltages  to  values from  0  to  4096,  with  2048
   corresponding  to  0V.  Other  cards  generate values from -2048 to
   2047 with a 0V value of 0.  Still  other cards give you a choice by
   having switches  on the card that you can  set.  It really  doesn't
   matter which kind of card you have.  Just  make  sure you tell EMON
   the proper values for your card.

þ  NoiseRangeToIgnore

   This parameter is  a percentage  of  the total ADC card range above
   and  below the value of  AdcValueAtZeroVolts.  Signals  within this
   zone will not be counted toward the decision to  save a quake file.
   For example if your  ADC returned values from 0 to 4095 with a zero
   value of  2048, specifying NoiseRangeToIgnore = 10  would result in
   EMON ignoring any points within a range of  10% (10 * 4096 / 100  =
   409.6, rounded  to  410) above  or below 2048.  So  any data points
   within a range  of (2048-410) to (2048+410) would be ignored, while
   data points outside this zone would contribute toward the  decision
   to save a quake file.  A typical value in a noisy environment might
   be 10-15.  In a quiet area, 1-3 is possible.

þ  SampleCountToSaveFile

   This is the number of samples  outside the noise zone  that must be
   observed before a quake file will  be saved.  This prevents lots of
   junk files being saved when only one or two points  above and below
   the noise zone are observed.  Typical value might be 50 or 100.

þ  SamplesPerDataPoint

   Multiple  ADC  samples  can be averaged  to  obtain one data point.
   This  provides limited smoothing if you are in a noisy environment,
   but its  biggest  benefit is to give you a  way to control how many
   samples  are   taken  per  second.  EMON  does  not  delay  between
   obtaining  samples, so the only way to slow down  the sampling rate
   is  to  tell it  to  make  each data point  an  average  of several
   samples.

   The fastest sampling rate is achieved  by setting  this value to 1.
   If this  is not fast enough you  either need a faster PC, a  faster
   ADC card or both.  However, sampling at the  maximum  rate may have
   some of the following drawbacks (especially on a faster PC):

   -  Each  file  may then contain only 5-10 minutes worth of data, so
      you will have many more files to deal with.

   -  You  may find  that distant events span  multiple  files,  which
      means you will have to use MSPLICE to combine the files later.

   Try  to achieve a sampling rate of about 10-20 per  second.  On  an
   XT-class machine you may have  to tell EMON  to average 5-8 samples
   for each data point to achieve this.  If you are running EMON  on a


                                              Software description  26






   286 or faster machine (AT-class) you may need to average as many as
   40-50 samples for each data point to achieve a final  sampling rate
   of 10-20 per second.  The  actual sampling rate is displayed on the
   EMON screen.

þ  StationName

   Specify up to 15 characters  for  your  station  name.  Only single
   blanks  are allowed in the name.  This  information is  placed into
   each quake file as it is saved.

þ  StationID

   Specify a three character ID  identifying your station.  This  will
   be used as the file name extension (".xxx") on all files saved.

þ  RecordingLatitude

   Enter the latitude of your station, with up to three decimal digits
   of  accuracy (fewer  is OK  too).  Use  positive values if you  are
   north of the  Equator, negative  values if  you are south.  If your
   map provides latitude only in degrees, minutes and seconds you will
   have  to  convert  to degrees.  For example, 16  degrees 30 minutes
   North latitude would be entered  as  16.5,  since 30 minutes is one
   half of a degree.

þ  RecordingLongititude

   Enter the  longitude  of  your  station,  with  up to three decimal
   digits of  accuracy (fewer is OK too).  Use positive  values if you
   are east of Greenwich, negative values if you are west.

þ  DisplayLines

   Enter the number of lines of data to display  on  the screen if you
   wish  a  real-time  display  of   data.  Entering  0  disables  the
   real-time display.  Only  odd numbers are acceptable.  If you enter
   an even number, EMON rounds it up to the next higher odd number.

þ  DisplayCompression

   Enter a number to use as a vertical compression factor for the EMON
   real-time  display.  The  higher this  number, the more  compressed
   each line of the display will be.  Generally a value of 10-25 works
   well.  The  number  you will need to get a good display will depend
   on the gain of your amplifier and  the range  of voltages generated
   by your seismometer.

þ  SavePath

   This is the DOS  "path" that EMON  will use  to locate the disk and
   directory in which to save quake files.  It can consist of

   -  just a  drive letter (for example, C:) in which case the current
      directory for that disk is assumed,


                                              Software description  27






   -  just  a  directory (in which case the named directory is assumed
      to be a sub-directory in  the  current directory on  the current
      drive, or

   -  a fully qualified combination of drive and directory.

   The directory must exist.  If it does not already exist at startup,
   EMON  will issue  a warning message  and terminate.  The  following
   examples are all acceptable:

SavePath           Meaning
----------         ----------------------------------------------------------
C:                 Use current directory on C drive
C:\                Use root directory on C drive
QUAKES             Use QUAKES (sub-)directory on current drive and directory
C:\QUAKES          Use QUAKES directory on C drive regardless of current dir
C:\QUAKES\         Same as C:\QUAKES
A:                 Use current directory on A drive
B:\                Use root directory on B drive

   The following examples are not  acceptable since they are not valid
   DOS paths:

A
C::
C\

þ  TemporaryBufferSize

   If  you  look into the  Appendix  in  which  the program  logic  is
   described, you'll  see  how  the Temporary Buffers  "A" and "B" are
   used.  Unless you care how often EMON examines the counters related
   to  quake  signals,  leave this  at  4000.  Acceptable  values  are
   1000-8000.

þ  UserCommand1

þ  UserCommand2

   Here you specify two  commands  which  can be executed  against the
   currently marked file on the screen.  Data  collection is suspended
   during the execution  of  a  UserCommand.  Place  the "/" character
   wherever you  would  like  the name of the file to  be substituted.
   For example, if the on-screen file marker were  pointing  at a file
   named 93066ACN.TBJ, the following substitutions would be made:

UserCommand             Actual command executed
-----------             -----------------------
QUAKEVU /      ===>     QUAKEVU 93066ACN.TBJ
QUAKEVU / /Q   ===>     QUAKEVU 93066ACN.TBJ /Q
COPY / A:      ===>     COPY 93066ACN.TBJ A:
MYBAT /        ===>     MYBAT 93066ACN.TBJ

   In  the first example above, the QUAKEVU program will be invoked to
   view  the  file.  Your  PC must  have enough "conventional  memory"


                                              Software description  28






   (i.e.  memory  below  640K) to  allow several  large programs to be
   active at one time,  or  you  may get  an "out  of memory" message.
   "Memory maker" utilities which  move portions of DOS above the 640K
   line may help you, but I  have  not tested them.  Examples might be
   QEMM and MemMaker.

   In the  second  example  above,  QUAKEVU is invoked  with the /Q or
   QuickDisplay option.  This tells QUAKEVU to display only every 10th
   point in the file.  On slower PCs this can give you a quick idea of
   whether the file contains anything interesting.

   In  the third example above,  the file is  to be copied to  the  A:
   drive.

   In  the  last  example  above,  the  user  has written a  BAT  file
   containing multiple DOS  commands, and  passes  it the name of  the
   marked file as its first parameter.

þ  ADCOffset

   This  is  a constant  value  to  be  added  to  each  sample taken.
   Negative numbers are  acceptable also.  This can  be handy  if your
   amplifier does not have a "zero" or "level" adjustment and you want
   to center the signal on the screen.

þ  ADCProgrammableGain

   Certain  ADC  cards  contain  onboard  amplifiers   whose  gain  is
   controllable by the software.  The  Real Time  Devices DR110 is one
   example.  This card supports  gain of 1, 10 and 100.  This value is
   ignored if the ADC card you are using does not support programmable
   gain.



EMON MAIN SCREEN

The EMON main screen is shown below.



















                                              Software description  29






ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³                                                                    ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


  Figure 9. EMON typical screen display



Header area

The first  line shows  the current date  (in standard and Julian form)
and  time,  the  version of EMON  you are running,  and  the  address,
channel and orientation of the seismometer currently being monitored.

The second  line  shows your  location and station  id,  latitude  and
longitude of  your station, and which of  the  three  internal buffers
("A", "B"  or  "Q") is being filled.  The program  alternates  between
filling  the "A" and "B" buffers until a  quake has been detected.  At
this time it switches to filling the "Q" buffer.

The third line displays the sampling rate in samples per second.  This
line (along with the time of day) is updated only every few seconds to
avoid slowing down the sampling rate.


Seismometer output display area

This area contains  a trace of the output of the seismometer.  You can
specify  how many lines  of trace it is to  show in the OPT file along
with the vertical scale.  The large tick mark on the left  edge of the
display  box shows where  the line  sould  be  when there is no  quake
activity.  The  small tick marks above  and  below this represent  the
upper and  lower  boundaries  of the  "noise zone".  If you change the
size  of the noise zone with  the F4  key  (or editing the  OPT file),
these markers will be adjusted to the new size.


Filename display area

This area shows  the files that  have been  saved  since  program  was
started.  For each file the file name, date and time are shown.  There
is also  a number between  1  and  100 which  describes  the  relative
intensity of the quake  record contained in the file.  (A value of 100
simply means  that the ADC card  recorded a signal  which  reached its
maximum  range.  Lower  numbers  signify  correspondingly  lower  peak
signals.)  This is to give you a rough idea of the size  of  the event
in the file.

A  small marker is always in front  of one of the file names.  You can
move this  marker with the up  and down arrow  keys.  The  UserCommand
keys always operate on the file with the marker in front of it.

All of the actions you can take from the keyboard are described below.



                                              Software description  30






EMON KEYBOARD ACTIONS

Up Arrow / Down Arrow

Use the  up and down arrow keys to select the file you wish to operate
on with the UserCommand  keys.  See  the  description  of the EMON.OPT
UserCommand1and UserCommand2parameters for further information.

F1 - Erase Current File

Erases the file currently  being pointed to on the screen.  You  would
generally use this  key  only  after  first  examining  the  file with
QUAKEVU, and copying all or part of it to another disk.  Copy the file
first if you want to keep it!

F2 - Turn On/Off Data Trace

The data trace shows the digitized value of each sample taken.  It  is
useful for debugging the A/D converter, or understanding noise levels.
If trace is off, pressing this key turns it on, and vice versa.

F3 - A/D Conversions Per Sample

This value is  the number  of separate  analog-to-digital  samples  to
average to get one  data point.  In  noisy environments, some  control
over noise  can be obtained by averaging  several samples, but  at the
cost of  slowing down the sampling  rate.  On  the  other hand, if you
wish to slow down the sampling rate, just specify a number larger than
1 for this parameter.  Initial value specified in EMON.OPT.

F4 - Noise Zone Width

Percentage above and below the "zero volts" value of the A/D converter
that defines  the  "noise zone".  Only samples outside this noise zone
will count toward the decision to save data to disk.

F5 - DOS command

Single DOS commands can be entered, or you can just press ENTER to  be
placed at the DOS prompt.  Typing EXIT returns you to EMON.

F6 - Save path:

Drive and path to be used  when saving  data  files.  A  hard drive or
1.2Mb floppy disk are recommended.  It  is possible to save files to a
5 1/4"  floppy, but only 7 files fit on a  standard 360K disk.  If the
disk  fills  up,  you  will  be prompted  to  insert a  disk with more
available space.  Sampling will  not resume until the data  file  just
obtained has been successfully saved to disk.

F7 - Display Next Device

When more than one seismometer  is  being monitored, pressing this key
will rotate the display among the devices.



                                              Software description  31






F8 - <UserCommand1> <File>

F9 - <UserCommand2> <File>

This key executes a command against  the  listed file.  The command is
specified  in  the  UserCommand  parameters  in EMON.OPT.  The  string
"<File>" is replaced by the name of the file currently marked with the
">" character on the screen.

F10 - Safe Quit

Return to DOS.  If a quake is in progress,  you will be asked if it is
acceptable  to discard  the data currently  being  collected.  If  you
reply "n",  the  current  data  will  be  saved in a "short" data file
before exiting.


ADC BOARDS SUPPORTED

EMON currently supports the following ADC data acquisition boards:

þ  IBM Data Acquisition and Control Adapter (12-bit)

þ  MetraByte DAS-4 (8-bit)

þ  MetraByte DASH-16 (12-bit)

þ  A  homemade board based on  the Real Time Devices PD-100  prototype
   board  for  the  IBM  PC, and the  Burr-Brown ADC674 analog-digital
   converter (12-bit).

þ  Alpha Products AN-146 A/D converter (12-bit).

þ  A homemade board based on modifying the PC parallel printer port to
   be a bi-directional I/O port.

þ  PC-Lab 714 SuperCard

þ  PC-Lab 711S

þ  Real Time Devices DR112 (13-bit)

An  entry in the OPT file allows you to  specify the type of board you
are using.

If  you  have  a  different model of  data  acquisition board,  please
contact me and I will be glad to add support for it if I can.


DISPLAYING QUAKE FILES WITH QUAKEVU

The QUAKEVU  program  displays  the  quake files captured by the  EMON
program.  It uses the  Color Graphics Adapter (CGA) in high resolution
(640x200) mode.  This is equivalent to SCREEN 2 in IBM BASIC.



                                              Software description  32






Note: If you are running QUAKEVU under DOS version 3.1 or higher,  you
must issue the DOS command "GRAPHICS" or "GRAFTABL" once each time you
power-on or re-boot the  machine.  If you do not  execute this command
before running QUAKEVU, the screen will look very strange with lots of
fuzzy square characters in the menus.  DOS  began  to require  this in
version  3  as part of their support for languages other than English.
If you find  you have this problem,  the simplest solution would be to
add  a line  with  the proper command  to your PC's AUTOEXEC.BAT file.
QUAKEVU will remind you when it starts if you need to run the GRAFTABL
command but have not done so.



QUAKEVU FEATURES

Functions supported by QUAKEVU are:

þ  Multiple  files  from  the same event (from  the  same or different
   recording stations) can be displayed simultaneously

þ  Mouse support with pull-down menus

þ  Online help

þ  Variable scale, on both X (Time) and Y (Amplitude) axes

þ  Interactive P- and S-wave identification via graphic pointers

þ  Automatic  epicenter distance and travel time calculations as the P
   and S pointers are moved

þ  Expanded view ("zoom") on a subset of the data in a file

þ  Ability to create a new data file containing only a subset  of data
   in the original file (and a comment if you wish)

þ  Connect data points with lines, or plot as points only



MOUSE INTERFACE TO QUAKEVU

If your  PC  has a mouse,  you  can  use  it  to  do  all of the above
functions via  pop-down  menus.  Several pop-down  menu  items  list a
keyboard function key (like F1  or F2) that does the same thing as the
menu bar.  You can use either one.


ARROW KEYS WHILE ZOOM'ED

If  you  are zoomed in on  a small section of a  file, you can use the
left and right keyboard arrow keys to move left and  right through the
file.  Each keypress moves one screen left or right.




                                              Software description  33






Further help is available in the program.  Enter QUAKEVU ? for details
or select HELP while running the program.


PRINTING THE SCREEN FROM QUAKEVU

Use the Shift-PRTSC key to print the screen if you want to save a hard
copy.  However, the DOS Print Screen function prints only in character
mode  and QUAKEVU runs  in  graphics  mode.  Luckily, DOS  supplies  a
command called GRAPHICS which takes care of this problem.  Execute the
GRAPHICS command  once each  time you power-on your  PC.  Once you run
this command, the  Print  Screen key will  print your QUAKEVU  screens
properly.  As with the GRAFTABL command the easiest solution may be to
add the GRAPHICS command to the AUTOEXEC.BAT file of the  PC where you
usually run QUAKEVU.


QUAKEVU EXAMPLE

Let's use QUAKEVU  to examine a  recording  of  a recent magnitude 6.0
earthquake  in  Hokkaido, Japan  on January  19,  1993.  This  was  an
aftershock  of the large magnitude  6.6  quake  that caused tremendous
damage in Hokkaido on January 15.

For this  example we'll assume we're using an older, slower  model PC,
so we'll invoke QUAKEVU with the QuickDisplay option (/Q) as follows:

        QUAKEVU 93019OIN.TBJ /Q

The  /Q option speeds up the display on  slower  PCs  by plotting only
every  10th sample and not connecting the points.  However,  the rough
outline you see is usually enough to  let you zoom in on  the  area of
interest.  Then you can turn  off the QuickDisplay  option to  see all
the details of the quake.

If  you  are  running QUAKEVU on a PS/2 with a 286 or faster processor
you will probably never need to use the /Q option.




















                                              Software description  34






Figure 10 on page  36  shows  the QUAKEVU initial  display.  Even with
only the rough outline displayed, we can see which area of the display
contains the  interesting  parts of the  earthquake  record.  We  have
bracketed this area by  choosing  Screen/Left Marker (or  pressing F4)
for  Zoom  and Screen/Right Marker for Zoom (or  pressing F4 a  second
time) and  placing the brackets around  the area of interest.  We  are
about to click on Zoom (or press F4 a third time).


















































                               Software description  35






ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Figure 10. Initial QUAKEVU display  using  QuickDisplay
           (/Q) option


In Figure 11 on page 37  we have zoomed  in  on  the area of interest,
and are still using QuickDisplay to speed up  the  drawing.  (We  have
also expanded the vertical scale from 55 to 10  to expand the trace in
the vertical direction.)  Now that we have the interesting part of the
trace on the  screen,  let's  turn  QuickDisplay  off and "connect the
dots" to see the actual record as it would have  been  recorded  on  a
chart recorder.












































                               Software description  36






ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Figure 11. Zoom display of the area of interest.


In Figure 12 on page  38  we can now see for the first time the actual
earthquake record.  You  can  begin to see  the arrival of the P waves
(not  very  distinct  due  to local noise), the S  waves (first  large
vertical  waves, quite distinct)  and other waves (L waves, the second
large vertical wave group).

Now let's tell QUAKEVU where we think the P and S wave arrivals are.













































                               Software description  37






ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Figure 12.  QUAKEVU screen after  turning  QuickDisplay
           off


Now in Figure 13 on page 39  we have selected P/S Waves and placed the
P and S markers at our best estimate of  the P and S arrivals.  Notice
that as we move the pointers, QUAKEVU calculates  the origin  time and
the distance from  the  recording  station to the  earthquake location
based on our placement of the  P and  S markers.  In this example  the
calculated  origin time of  14:40:23  does not  exactly match the true
(USGS) origin time of 14:39:27 since the PC clock was off by about one
minute.  However the distance estimate (640 km)  matches closely  with
the actual distance to the earthquake location.  (The  actual distance
was  determined by using the  HOWFAR program to calculate the distance
between  the  recording  location  and the  earthquake  location.  The
actual latitude and longitude  of the earthquake was obtained from the
U.S. Geological Survey and newspaper stories.)






































                                              Software description  38






ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Figure 13. Origin time & distance calc. using P/S pointers



SAVING A SUBSET OF THE ORIGINAL FILE

At  this  point you will probably want to use File/Save (F8) to save a
smaller size file  containing  only the portion of  the  original file
currently  being displayed.  Select  File/Save (or  press F8) and  you
will  be prompted to specify up to 7  characters of a file name.  (The
8th character and the file extension are copied from the original file
name).  You can enter names like the following:

  a:*            Saves file on a: drive with same name as large file
  b:myquake      Saves file as b:myquake.lll (where lll is station ID)
  \quakes\*      Saves file in QUAKES directory with same name
  myquake        Saves file in current drive/directory as myquake.lll
  *              Replaces input file (large) with subset file (small)



PRINTING THE SCREEN CONTENTS

You might want to print what is on the screen to have a hard copy  for
your  files.  To  print the screen contents, you must have issued  the
DOS  command "GRAPHICS" in the  DOS session  before  entering QUAKEVU.
This command tells DOS that all future PrintScreen  key presses should
assume the screen is in graphics mode (like QUAKEVU uses), rather than
just as text.  If  you  did  not issue  the  GRAPHICS  command  before
invoking QUAKEVU, you  can do so now via  the  DOS  Command key.  Then
just press the Shift-PrtSc key and DOS will print your screen image on
the printer.  Note - some laser printers  will not properly print this
type of screen.  You may  have  to  use an "old-fashioned"  dot-matrix
printer or some other type of screen-capture program.


DATA FILES

Quake data files contain exactly 25,000 data  points when  first saved
to disk by  EMON.  As mentioned in the QUAKEVU example, you can create
a  smaller  file  containing  just  the  interesting  portions   of  a
recording.  First, load  the  file  into  QUAKEVU.  Next, use the Zoom
function,  and perhaps  the right and left arrow keys  (or  CTRL-arrow
keys), to  show just  the interesting part of the  file on the screen.
Finally, use the  SAVE  function  to  save just the  part  of the file
showing  on  the  screen.  It  is  a  good idea  to do this if you are
uploading the  file  to a BBS  - it can save telephone charges  if you
upload smaller  files, and saves other people money when they download
your files to their PCs.  During the save process you will be asked if
you want to add descriptive information which  you may have determined
through other sources to reserved spaces in  the file.  These might be
things like the true origin time, or a comment.  For  files  saved  by
EMON  V6 or  later you will  be asked  if you want  to  add additional


                                              Software description  39






information like depth, latitude and longitude.


DATA FILE NAMES



Data file names for files created by EMON V5

Data file names are designed to  pack as much information  as possible
in  the eleven characters  that DOS allows us to use.  The  format for
quake file names is YYDDDHMO.LLL, where:

þ  YY is the year

þ  DDD is  the day of the year (YYDDD is  sometimes called the "Julian
   date")

þ  H is a letter between A and X corresponding  to  the hour in  which
   the first sample in  the  file was obtained.  For example,  a  file
   with "A"  in this position contains data from sometime in the first
   hour after midnight.

þ  M  is  a  letter  between A  and  L corresponding to  the  5-minute
   interval in the hour during which the first sample in  the file was
   obtained.  A file with "C" in this position  was collected starting
   at around 10 minutes after the hour.

þ  O is the orientation of the seismometer - N for a device whose boom
   was oriented North-South, E for one oriented East-West, and Z for a
   vertical unit.  You  supply this  description  in  the OPT file for
   each device you monitor.

þ  LLL  is the 3-character location code you  supply in the  OPT file.
   This code identifies  your monitoring station.  It should be unique
   among the groups with which you share data.

As an example, a file saved on January 3, 1992 at 1:08am in Wappingers
Falls, NY on a N-S oriented device might be named 92003BBN.WPF.


Data file names for files created by EMON V6

The pattern  for  data file names  created by EMON V6 is chosen by the
station  operator.  Please  see  EMON  Options  File  on page 16 for a
description of the file name patterns which are possible.











                                              Software description  40






BIBLIOGRAPHY



GENERAL BACKGROUND

Bolt, B. A..  Earthquakes.  W. H. Freeman, 1988.

Gere,  J.  M.  and H. C. Shah.  Terra  Non  Firma,  Understanding  and
Preparing for Earthquakes.  W. H. Freeman, 1984.

"Earthquakes & Volcanoes", published bimonthly by the U. S. Geological
Survey.  Available from: Sup't.  of  Documents,  U. S. Gov't  Printing
Office, Washington, DC 20402.


SEISMIC MONITORING STATION PRACTICES

World  Data  Center  A for Solid  Earth Geophysics,  September,  1979.
Manual of Seismological Observatory Practice, Report SE-20.  Available
from:  United States Dept.  of  Commerce,  National  Oceanographic and
Atmospheric  Administration,  National  Geophysical Data  Center,  325
Broadway, Boulder, Co. 80303


HOME SEISMOMETER CONSTRUCTION AND DESIGN

Various older  Scientific American "Amateur Scientist" columns:  June,
1953, July, 1957, May, 1961, and August, 1970.

"The Amateur Scientist: A sensitive mercury tiltmeter that serves as a
seismometer", Scientific American, November, 1973, pp. 124-129

"The Amateur Scientist: Electronic stratagems are the  key to making a
sensitive  seismometer",  Scientific  American,  September,  1975, pp.
182-187

"The Amateur Scientist: How  to  build a  simple seismograph to record
earthquake  waves  at  home".  Amateur  Scientist  column,  Scientific
American, July, 1979,  pp. 152-161 (Plus a correction to the amplifier
schematic in the Amateur Scientist column, August, 1979)


EARTHQUAKE INTERPRETATION

Simon,  Ruth L.  Earthquake  Interpretations,  A  Manual  For  Reading
Seismograms.  Los Altos, Ca., William Kaufman, Inc., 1981.

Jeffreys, H. and K. E. Bullen.  Seismological Tables.  Smith & Ritchie
Ltd., Edinburgh, 1967.







                                                      Bibliography  41






PERSONAL COMPUTER DATA ACQUISITION

Webster,  E.,  1986. How To Use  Your  BBC Computer As a Cheap Storage
Oscilloscope.  Phys. Educ. 21, pp. 119-122

Ciarcia, S.  A., "Computers on the Brain:  Clever  signal  amplifiers,
noise rejection and A/D conversion are all part of the HAL EEG", Byte,
June, 1988.


SEISMIC SOFTWARE DESIGN

Allen,  R.,  1982.  Automated Phase Pickers:  Their  Present  Use  and
Future Prospects.  Bull. Seis. Soc. Am. 72(6), pp.S225-S242

Goforth,   T.  and  E.  Herrin,  1981.  An  Automatic  Seismic  Signal
Detection  Algorithm Based On The Walsh Transform.  Bull.  Seis.  Soc.
Am. 71(4), pp.1351-1360


SEISMOMETERS IN THE CLASSROOM

Barker,  G. "A Working Seismograph For The Classroom".  Michigan Earth
Scientist, Michigan  Earth  Science  Teachers  Association, September,
1983.

Barker, G. "Calculating the  Size and Properties of the Earth's Core".
Michigan Earth Scientist, Michigan Earth Science Teachers Association,
June, 1984.




























                                                      Bibliography  42