This file contains the information for how to change the scanner
configuration settings.


1. INTRODUCTION
~~~~~~~~~~~~~~~

  During the installation of Mustek TWAIN Data Source, the scanner settings
  (i.e., IRQ, DMA and I/O address settings) will be automatically updated
  in the WIN.INI file. However, there are instances when you may need to
  change the IRQ, DMA or I/O address setting to avoid a hardware conflict.


2. HOW TO CHANGE THE SCANNER SETTING
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

  To change the scanner settings, please execute the SCANTEST module which
  can be found in the Mustek TWAIN group icon and follow the onscreen
  instructions.

  Note: To change the I/O address setting for some scanner interface card,
        you should change it by changing the I/O address switch setting on
        the scanner interface card and the Scantest module will detect the
        new setting automatically. Please refer to the included manual for
        how to change the I/O address.


3. CALIBRATE THE SCANNER
~~~~~~~~~~~~~~~~~~~~~~~~

  For best scanning results, we recommend that you calibrate the scanner
  the very first time you use it. The calibration procedure involves
  scanning a white sheet of paper and adjusting the brightness control
  until you get a Calibration OK message. After this you don't need to
  calibrate again unless you notice a significant decrease in scan quality.

  To calibrate the scanner, the steps are:

     1.Set the Brightness Control of your scanner to the middle position.

     2.In the Hand Scanner dialog box, click the Preference button.
       The Preference dialog box appears.

     3.Click the Calibration button and follow all onscreen instructions.


4. TWAIN COMPLIANT
~~~~~~~~~~~~~~~~~~

1. ABOUT OmniPage OCR (TWAIN-Compliant Version)

   Please modify the SCANMGR.INI under the Windows directory as below:

   1.1 Set
      ...
      TWAINDS=Mustek Hand Scanner II
      ...

   1.2 Add
      ...
      [Mustek Hand Scanner II]
      SHOW_UI=1    --------------> Show User Interface
      INVERT=1     --------------> Invert image
      AUTO_BRI=0   --------------> Text(LineArt) Scan Mode
      DPI=1        --------------> Resolution = 300 dpi
      DOCTYPE=0    --------------> Document Type = Black & White
      ORIENT=4     --------------> Orientation = Landscape(L to R)

   1.3 Switch scanner to TEXT scan mode, 300 DPI.

2. ABOUT GO-CR V1.3 & V2.1

   Merge function is not supported for this application.