Note: We didn't include the INSTALL program with this shareware
	release of the ARF AV utilities; there were simply too many varia-
	bles to consider.  The correct order in which to do all of these
	things is:  Use INJECT.COM to inject your program files, then use
	LOAD.COM to build a PRO-BOOT diskette.  Boot onto the PRO-BOOT
	diskette and install the ARF AV partition.  Finally, run
	ARFBUILD.COM to construct the ARFMAIN.BIN driver.

	Here are brief instructions for each program:

	Installing INJECT.COM
	ßßßßßßßßßßßßßßßßßßßßß

	To install the INJECT module to executable files in one subdirectory
	use the following command:

	INJECT *.*

	This will create backup files and leave them in the current directory

	To remove the INJECT module from executable files in one subdirectory
	use the following command:

	INJECT *.* -r

	The above examples assume that INJECT is in the same subdirectory
	as the files. If this isn't the case, add the drive and path to
	the file specifier (i.e. INJECT C:\DIRNAME\*.*).

	You should read INJECT.DOC for a complete list of command line
	options.





								Page 2

	Installing PRO-BOOT
	ßßßßßßßßßßßßßßßßßßß

	First, take a diskette that doesn't contain any information that
	you will mind losing and put it in drive A:. The file LOAD.COM
	should be located on drive C:. Run LOAD.COM. Enter an indentification
	string when asked that will help you identify that computer in the
	future. After LOAD.COM has finished, remove the PRO-BOOT diskette and
	write protect it. For a 3.5" diskette, turn the diskette over so the
	back of it faces you. In the lower right corner you'll see a small
	button that will slide up and down. Slide the button down towards
	the bottom of the diskette (the end that doesn't go into the computer).
	MAKE SURE YOU LABEL THE DISKETTE!

	Now, put the diskette back in drive A: and boot or restart your
	computer. After reading some on screen information, you'll come to a
	menu with the following choices:

	
	   A) Abort - will continue boot process from current partition     
	   1) Reinstall original partition                                  
	   2) Test original partition                                       
	   3) Install ARF Anti-Virus partition                              
	   4) Test ARF Anti-Virus partition                                 
	   5) Install stock DOS compatable partition                        
	   6) Test stock DOS compatable partition                           
	
	Our recomendation is to select item 4 and test the ARF  Anti-Virus
	partition. If that works, reboot with the PRO-BOOT diskette in
	drive A: and select item 3) to install the anti-virus partition.
	After this, remove the diskette and put it in a safe place.

	To remove PRO-BOOT, simply boot your computer (or start it) with
	the PRO-BOOT diskette in drive A:. Select item 1) to reinstall your
	original partition. 

	If you ever get a warning from PRO-BOOT that INT 13h has changed,
	BIOS memory has changed or the MBR has changed, reboot your
	computer with the PRO-BOOT diskette in drive A: and install the
	Anti-Virus partition again.

	If you install a new operating system or if you repartition your
	hard drive, it will be necessary to create a new PRO-BOOT diskette.
	You'll have to start this process all over again.




								Page 3

	Installing the ARFMAIN AV Driver
	ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Make sure that you've run PRO-BOOT first, and have installed the
	desired partition, if any; you want to be through with all system-
	level changes before building the driver.

	The driver is constructed by running ARFBUILD at the DOS prompt.
	Here's the quick and dirty procedure.

	1.  Temporarily rename your CONFIG.SYS and AUTOEXEC.BAT files to
	    CONFIG.BAK and AUTOEXEC.BAK.  Switch the PC off, wait a
	    moment, and switch it back on.  Don't use CTRL-ALT-DEL.

	2.  Run ARFBUILD at the DOS prompt.  The driver, ARFMAIN.BIN, will
	    be created in the current subdirectory.

	3.  Copy the driver into your root (C:\) subdirectory.

	4.  Rename CONFIG/AUTOEXEC.BAK to their original .SYS and .BAT
	    extensions.  DON'T reboot just yet ...
	
	5.  Using DOS's EDIT program (or any other suitable text editor),
	    add one of these two lines to the end of your CONFIG.SYS file:

	    Under DOS 5.0 or better -- "DEVICEHIGH=ARFMAIN.BIN"
	    Older versions of DOS   -- "DEVICE=ARFMAIN.BIN"
	    
	    (Don't enter the quote marks.)  
	    
	6.  Reboot the computer; the driver will be loaded in memory, and
	    begin protecting the system.  If you get error messages, or
	    have other problems, see ARFBUILD.DOC.