* Multi-CALL 1.xx Callback Door for ANY DOS BBS
* Copyright 1995 by Michael Robinson. All rights reserved.

* Information for software developers

Multi-CALL 1.xx reads and writes 3 different BBS door drop file formats:

  DOOR.SYS .......... Used on many BBS systems.
  DORINFOx.DEF ...... Used on many BBS systems.
  SFDOORS.DAT ....... Used on Spitfire BBS.

Multi-CALL reads one of these files to get the com port number, node number,
connect speed, user name, time left, address, phone number, password,
security level, graphics mode, user record number, if call is error
correcting, and time of the call. (Of course, it can only read what is
there. DORINFOx.DEF does not have all this information.) The door drop file
used is specified as the first parameter on the Multi-CALL command line. The
only information written to these files is the caller security level and
time left. See the included DOORSYS.TXT file for a detailed breakdown on
exactly which lines are read and written.

Multi-CALL 1.xx reads and writes to BBS specific file formats:

  USERREC.BIN  (binary) for Wildcat 4.xx
  USERINFO.DAT (ascii ) for Wildcat 3.xx
  USERS.SYS    (binary) for PCBoard
  LASTUSxx.BBS (binary) for Maximus 2.xx (file size = 240 bytes)
  LASTUSxx.BBS (binary) for Maximus 3.xx (file size = 460 bytes)
  EXITINFO.BBS (binary) for RA 2.xx and ProBoard
  USER.LST     (binary) for TAG 2.7

The program does NOT read/write any of these files unless the appropriate
command is specifically set in MCALL.CFG. The use of these files is
optional. If used, Multi-CALL reads the caller security level, password,
password CRC, phone numbers, credit, and points from these files. (Of
course, it can only read what is there. Some of these files don't have all
this information). The door drop file is read first (required) and then the
BBS specific file is read (optional). If both files contain the required
information, the value from the BBS specific file is used. The only
information written to these files is as follows:
                                                                    Download
                       Security  TimeLeft  Credit  Comment  Points  Security
                       --------  --------  ------  -------  ------  --------
USERREC.BIN   Wildcat    YES       YES       NO      YES     NO       NO
USERINFO.DAT  Wildcat    YES       YES       NO      NO      NO       NO
USERS.SYS     PCBoard    YES       YES       NO      YES     NO       NO
LASTUSxx.BBS  Maximus 2  YES       YES       YES     NO      NO       NO
LASTUSxx.BBS  Maximus 3  YES       YES       YES     NO      YES      NO
EXITINFO.BBS  RA/ProB    YES       YES       YES     YES     NO       NO
USER.LST      TAG 2.7    YES       YES       YES     YES     YES      YES

When a piece of information is listed as NO above, that information is
never written to that file. This is because that particular file format has
no place to put that information. When listed as YES, the information MAY
be written to that file depending upon whether or not the optional
configuration command governing that information is used in MCALL.CFG.
The program does NOT write any of the information unless the appropriate
command is specifically set in MCALL.CFG.

Multi-CALL also creates several different files which can be read by third
party utilities:

  CALLGOOD.x ------ Information on the last good callback.
  VERIFIED.LST ---- Permanent record of all good callbacks.
  TODAY.LST ------- Record of all callbacks (good and bad) today.


VERIFIED.LST and TODAY.LST

These are plain ASCII text files. The format of VERIFIED.LST and TODAY.LST
are identical. There is one line for each callback in this format:

203-924-5603  Mike Robinson  LOCAL       10:15:43 09-30-95  Shelton, Ct.

Each of the fields on the line is separated by a  character (ASCII #01).
If any  characters are embedded in the caller name or address,
(as supplied by the BBS in the door drop file) they will be replaced with a
blank (ASCII 32). The caller name is actually padded with blanks to a fixed
length of 36 characters. The padding is removed in the example shown above.
The field occupied by LOCAL above can be one of several possible values:

   LOCAL      
   LONGD      
   LOCAL FAKE 
   LONGD FAKE 

The length of the phone number and time/date field may vary, so I recommend
that you do NOT parse the line based on position. Use the  characters.
This is why I put them in there.


CALLGOOD.x

The CALLGOOD.x file is only created after a good callback. The x in the
file name is replaced with the node number. So for node 1, the file is
named CALLGOOD.1. This file is deleted during Multi-CALL startup. (Only the
file for the node being used is deleted.) This file currently has 6 lines.
I reserve the right to add lines in the future. Make sure that any
additional lines do not break your program. Here is a typical CALLGOOD.x
file:

203-924-5603
Mike Robinson
147
10
Shelton, Ct.
10:15:43 09-30-95

Line 1 above is the phone number as read from the door drop file. If the
caller changes this number, then whatever the caller typed in is shown
here. The format of this number is defined by the phone number mask on line
1 in LANGUAGE.LST.

Line 2 above is the caller name exactly as read from the door drop file.
No characters are replaced or stripped out.

Line 3 above is the number 147. This is the caller user record number in
the BBS users file. This number is read from the door drop file, so it is
possible that it is not correct. Use with care. Some BBS systems call the
first record number 0, while others call it record number 1.

Line 4 above is the number 10. This is the caller security level AFTER the
good callback. This may or may not be a change in security level depending
upon how the program is configured. If the security level is changed, then
this line shows the final changed value. On BBS systems that support name
type security levels, this line may be a text string.