D51 Version 2 USER'S MANUAL


                          8051/8052 Disassembler







                             Jeffery L. Post
                    22726 Benner Ave, Torrance, CA 90505


                              October, 1995


























             MSDOS is a trademark of Microsoft Corporation
             PCDOS is a trademark of International Business Machines




			TABLE OF CONTENTS


Introduction .................................................. page 1

Quick start ................................................... page 3

Command line options .......................................... page 4
    A option .................................................. page 4
    B option .................................................. page 5
    D option .................................................. page 5
    H option .................................................. page 5
    S option .................................................. page 5
    X option .................................................. page 6

Control file directives ....................................... page 7
    A directive ............................................... page 8
    B directive ............................................... page 8
    C directive ............................................... page 8
    F directive ............................................... page 9
    I directive ............................................... page 9
    K directive ............................................... page 9
    L directive ............................................... page 10
    R directive ............................................... page 10
    S directive ............................................... page 10
    T directive ............................................... page 11
    W directive ............................................... page 12

Format of Output File ......................................... page 13

Background .................................................... page 15

Technical info ................................................ page 16

Summary ....................................................... page 19

8051 register maps ............................................ page 21





								Page 1


                            INTRODUCTION

    D51 Version 2 is a significant improvement over D51 V1. Version 2
    allows the user to specify areas of the code to be disassembled
    as something other than executable code; ie: as ascii text, binary
    data, address tables, etc (see the section on control file direct-
    ives). You may specify such areas by means of an ascii text file
    with the same name as the file to be disassembled, but with an
    extension of CTL (for example: program.ctl controls the disassembly
    of program.hex or program.bin). By means of the control file, you
    can, by an iterative process, get a progressively more meaningful
    disassembly by modifying the control file based on examination of
    the output of previous passes of D51. You can also specify names
    for labels and symbols in the control file, resulting in a much
    more readable source file. A file named GENERIC.CTL is provided as
    a means to get the user started; just copy GENERIC.CTL to FILE.CTL,
    where FILE is the name of the file to be disassembled, and make
    appropriate changes. Labels and symbols are limited to six charac-
    ters, since most cross assemblers have this limitation.

    Like V1, D51 V2 still does not analyze the code; the user must do
    so and control disassembly via the control file. A code analyzing
    disassembler is under development (as of May, 1995). SD51 (for Super
    Disassembler 8051) will do static and dynamic analysis of the hex or
    binary file, and automatically determine which parts of the file are
    executable code, address tables, ascii text, etc. SD51 will likely
    not be public domain, but will be distributed either as shareware or
    as a commercial product (interested publishers can contact the author
    at the address given above).

    Unlike D51 V1, which was distributed as a public domain program
    without source code, Version 2 is being distributed with source code
    under the GNU General Public License (see the file COPYING for
    details). The author has benefited greatly from software distributed
    under the GNU GPL and wishes to thank those who have contributed so
    much by adding his own meager efforts to the large base of freely
    distributable software. It is the author's contention that software
    patents are an oxymoron; that although the United States Patent Office
    recognizes that mathematical algorithms are not patentable, they are
    too ignorant to recognize the fact that ANY software is expressable as
    a mathematical algorithm. The author specifically refuses to acknowledge
    the legitimacy of any software patents whatsoever. Copyrights, trade-
    marks and trade secrets are, however, another matter.

    In accordance with the spirit of the GNU General Public License, the
    following notice is added to this documentation:

    This program is free software; you can redistribute it and/or modify
    it under the terms of the GNU General Public License as published by
    the Free Software Foundation; either version 2 of the License, or (at
    your option) any later version.




								Page 2


    This program is distributed in the hope that it will be useful, but
    WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANT-
    ABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General
    Public License for more details.

    You should have received a copy of the GNU General Public License
    along with this program; if not, write to the Free Software
    Foundation, Inc., 675 Mass Ave, Cambridge, MA 02139, USA.

    The file COPYING contains the full text of the GNU General Public
    License, Version 2.

    The quick start section of this document gives some minimal informa-
    tion for users who are eager to try out D51. For best use of D51,
    however, you should read the sections on command line options and
    control file directives before proceeding.

    The section entitled 'background' describes the purpose of a dis-
    assembler, how a disassembler works (in basic terms), and the reasons
    you might want to use one. This section is intended for novice users
    but might be interesting to more advanced users.

    The technical info section covers disassembly techniques and gives a
    detailed description of D51 and its source code. This is intended for
    more advanced users who might want to modify or expand D51, or even
    create a disassembler for a different 8 bit processor. Those who peruse
    this section, and the source code, will see that the techniques
    employed in D51 are only applicable to processors that are limited to
    64K or less of program memory (most 8 bit processors).




								Page 3


                            QUICK START


    To disassemble a file called 'code.bin' or 'code.hex', type in (at
    the DOS prompt):

		copy generic.ctl code.ctl

    to create a control file for the disassembly, and then type:

		d51 code d

    A control file is not necessary for disassembly, but as will be seen,
    it will provide for a much more complete disassembly.

    If neither the 'b' option nor the 'h' option is specified, D51 will
    first search for a hex file and, if it is not found, then search for
    a bin file. D51 can be forced to look for only one or the other by
    specifying the (b)inary or (h)ex option on the command line:

		d51 code b d		for the file code.bin, or

		d51 code h d		for the file code.hex

    D51 will produce a file named 'code.d51' containing the disassembly of
    the 8051/8052 instructions in the original hex or binary file. It is
    very useful on the first few disassemblies to use the 'd' option, which
    adds a comment field to every line. The comment field contains the
    hexadecimal address of each instruction, the hex data for each byte in
    the instruction, and the ascii code for each byte of the instruction.
    Example:

		(opcode) (operands)	(address) (data)   (ascii)
		orl	a,#42h		; 0df6   44 42      DB

    This makes it easy to spot areas of ascii text or other nonexecutable
    code, and then modify the control file to tell D51 that these areas
    should be treated as some other kind of data on subsequent disassem-
    blies. Please see the section on control file directives for specific
    information.

    By examining the output file and then modifying the control file based
    on the information obtained, you can get a progressively better disas-
    sembly of your 8051 program. Generally, about half a dozen iterations
    of the disassembly are enough to produce a very readable source file
    that can then be modified and reassembled.




								Page 4


                       COMMAND LINE OPTIONS


    Command line options modify the operation of D51. They may be
    specified on the command line using either Unix style options:

	d51 -db filename

    or MSDOS style options:

	d51 /d /b filename

    Options may be entered in a freeform fashion (in any order or format)
    provided that any options preceeding the filename must begin with
    either a dash (-) or a slash (/). For example:

	d51 /db filename -x1000
	d51 filename -d b x1000
	d51 -d filename bx1000

    all mean exactly the same thing and will cause D51 to behave in
    exactly the same way.

    Command line options in Version 2 are:

    A OPTION (ascii macro):

	The A option tells D51 to change the db/defb pseudo op to the
        ascii macro for areas defined as ascii text. This will cause D51
	to include a macro definition in the disassembly output file that
	should expand to 'db' for the cross assembler. To use this option,
	your cross assembler must be able to handle macros, and in parti-
	cular, D51's macro format. If used in conjunction with the S option
	(see below), the S option must come first on the command line.

	There are some caveats regarding the ascii macro. The intent of
	this macro is to make ascii text easier to find in the output file.
	Once you're satisfied with the readability of the output file, you
	may want to run D51 once more without the A option to produce a
	file more digestible by your cross assembler.

	Some cross assemblers treat certain characters within a macro as
	special meta-characters. The Huntsville Microsystems A51, for
	example, regards the characters '#', '.' and '\' as special with-
	in a macro. If these characters occur in ascii text using the
	ascii macro of D51, the assembler will do strange and not so
	wonderful things with them. If this happens, just do not use the
	A option (by default, it is off).

	A problem that will be common with all cross assemblers is that
	D51 does not currently treat the single quote (') character




								Page 5


	differently than it does other characters within ascii text.
	Since D51 delineates ascii text (whether using the A option or
	not) with the single quote character, its presence in ascii text
	areas will cause problems. The only solutions to this right now are
	to manually edit the output file of D51 or to define the byte of
	the single quote as a binary byte in the control file (see the B
	control file directive).

    B OPTION (binary file):

	The B option forces D51 to read a binary file (extention .bin)
	instead of an Intel hex file (extention .hex). If neither the
	B nor the H option are specified, D51 will first search for a
	file with an extention of .hex, and if not found, will then
	search for a binary file with an extention of .bin.


    D OPTION (data in comment field):

	The D option tells D51 to include a comment field in each
	disassembled line. The comment field will contain the hexadecimal
	address of each instruction, the hex data for each byte in the
	instruction, and the ascii code for each byte of the instruction.
	Example:

		(opcode) (operands)	(address) (data)   (ascii)

		orl	a,#42h		; 0df6   44 42      DB

	This makes it easy to spot areas of ascii text or other non-
	executable code, and then modify the control file to tell D51
	that these areas should be treated as some other kind of data on
	subsequent disassemblies. Please see the section on control file
	directives for specific information.

    H OPTION (hexadecimal file):

	The H option forces D51 to read an Intel hex file (extention
	.hex) instead of a binary file (extention .bin). If neither the
	B nor the H option are specified, D51 will first search for a
	file with an extention of .hex, and if not found, will then
	search for a binary file with an extention of .bin.

    S OPTION (string pseudo op):

	This option tells D51 to generate the pseudo ops 'defb' and
	'defw' instead of 'db' and 'dw' for those cross assemblers that
	may require this. Most 8051 cross assemblers understand 'db'
	and 'dw', so these are the defaults for D51. Use this option
	for cross assemblers that do not recognize 'db' and 'dw'. If
	used in conjunction with the A option, the S option must preceed
	the A option on the command line.




								Page 6


    X OPTION (hexadecimal offset):

	This option causes D51 to add a hexadecimal offset to the address
	of every location in the code file. This may be useful for dis-
	assembling code that was read from the second (or subsequent) rom of
	a set of roms. For example, suppose that binary data was obtained
	from a set of 4K byte eproms (call them rom1 and rom2). Then the
	first file should be disassembled with the command line:

		d51 -d rom1

	and the second should be disassembled with the X option:

		d51 -d rom2 x1000

	The two files then can be combined into one and all references
	within the disassembled code will be to the correct addresses.




								Page 7


                       CONTROL FILE DIRECTIVES


    Control directives tell D51 to treat specified areas of the code
    to be disassembled as something other than executable code. The
    user specifies control directives by editing (with any text editor)
    a control file with the same name as the file to be disassembled, but
    with a file extention of .ctl (eg: program.ctl to control the dis-
    assembly of the file program.hex or program.bin). A generic control
    file called 'generic.ctl' is provided to get the user started. Copy
    'generic.ctl' to 'file.ctl' where 'file' is the name of the binary
    or Intel hex file to be disassembled, and modify as required based
    on the output of D51. Then run D51 again to get a more readable
    disassembly of the code.

    All directives consist of a character that specifies the type of data,
    followed by a hexadecimal number specifying the value or range of
    values of the data. In the case of a label or symbol directive, the
    hexadecimal number is followed by ascii text defining the label or
    symbol. See individual directives for examples. Labels and symbols
    are limited to six characters. All directives must be in the first
    column of the line. Everything following a semi-colon (;) is a comment
    and will be ignored by D51.

    Label and symbol directives differ in that a label refers to an
    address and a symbol refers to any 8 or 16 bit data. Therefore an
    opcode such as

	mov	r2,#data

    will cause D51 to search only the symbol table for a matching value
    whereas an opcode such as

	mov	dptr,#data

    will cause D51 to search the label table first, and if no matching
    value is found, to then search the symbol table.

    Single values are specified by entering just the value; ranges of
    values are specified by a start and stop address separated by a dash
    (-), or by a start address and count separated by a plus (+), ie:

	a 1000		tells D51 that the data at address 1000H is ascii
			data.

	a 1000-1010	tells D51 that the data from address 1000H to
			(and including) address 1010H is ascii data.

	a 1000+6	ascii text starting at 1000H for 6 bytes.




								Page 8


    Directives are processed in the order in which they are read from
    the control file. Specifying an area as ascii data and then later
    specifying it as data to be ignored (uninitialized data) will cause
    that area to not be disassembled at all. Care must be taken in
    specifying areas in the control file.


    A DIRECTIVE (address data):

	Specifies that the address contains a word value corresponding
	to an address for which a label should be generated. For example,
	a vector table may be located at address 0x1000 containing four
	entries. The user can modify the control file by adding the
	following entry:

		a 1000-1007

	This will cause D51 to generate the following output lines:

		dw	vec1
		dw	vec2
		dw	vec3
		dw	vec4

	assuming that the control file also contains entries for the
	values found at those addresses to generate the labels vec1
	through vec4. The addresses referenced will be flagged so
	that labels will be generated in the output file at those
	addresses.

    B DIRECTIVE (byte binary data):

	Specifies that the data is to be interpreted as 8 bit binary
	data. For example:

		b 1000-1007

	tells D51 that the data from address 1000H to 1007H should
	generate the line:

		db	0,1,2,3,4,5,6,7

	assuming that the data at address 1000H and up is 00H, 01H, etc.

    C DIRECTIVE (code data):

	Forces D51 to interpret the data as executable code. This may be
	necessary because D51 skips over strings of 00H or ffH bytes that
	occur since they are unlikely to be real code. However, sometimes
	programmers insert several NOPs for timing purposes.




								Page 9


    F DIRECTIVE (SFR label definition):

	Causes reference to an SFR (special function register) to
	generate a label for the specified SFR address. This is useful
	for naming SFR's for non-standard members of the 8051 family.
	For example, suppose that some manufacturer designs a new 8051
	variant and decides to use address efH as a new special function
	register called 'NEWREG'. Then by adding:

		f ef newreg

	to the control file, D51 will disassemble the opcodes f5 ef as:

		mov	newreg,a

	instead of:

		mov	0efh,a

	SFR label names are limited to six characters.

    I DIRECTIVE (ignore data):

	Tells D51 to ignore a range of addresses that may be initialized
	by the input file. This is useful when the input file is a binary
	file generated by an eprom programmer that dumps the entire eprom
	space. The valid data from a 4K eprom might only be, say, 3K in
	length. By adding

		i c00-fff

	to the control file, you tell D51 to not disassemble the data
	from address 0c00H to 0fffH.

    K DIRECTIVE (SFR bit definition):

	As with the F directive, you can give a name to a new SFR bit.
	If a new variant of the 8051 family adds a new interrupt, for
	instance, its enable bit in the IE register might be bit 6. By
	adding:

		k ae 6 newint	(ae is the address of IE.6)

	you define bit 6 of the interrupt enable register to be

		ie.newint

	Like SFR label names, SFR bit names are limited to six characters.




								Page 10


    L DIRECTIVE (label):

	Defines a label to D51. Labels are generated in the output
	disassembly file whenever a reference to the address is found
	and the label exists in the label table. Suppose that address
	0000H contains the code 01 43 (ajmp 0043H). Then the entry

		l 43 start

	in the control file will cause D51 to disassemble this code as:

		ajmp	start

	rather than:

		ajmp	X0043

	The code beginning at address 43H will then have the label
	'start' in the label field rather than the label 'X0043'. See
	the entry for the S directive for an explanation of the diff-
	erence between labels and symbols. Labels and symbols are
	limited to six characters.

    R DIRECTIVE (register definition):

	This directive specifies a name for an 8051 register. Direct
	accesses to registers will normally be disassembled as:

		mov	rb2r5,a

	in the case of register 5 of register bank 2. If the user
	determines that register 5 of bank 2 is being used as a loop
	counter, for example, he can give it the name loop by adding:

		r 15 loop

	to the control file, and the above code will be disassembled as:

		mov	loop,a

    S DIRECTIVE (symbol):

	Defines a symbol to D51. Symbols are output to the disassembly
	file whenever the value is encountered in the input file and the
	symbol exists in the symbol table. The user can specify a symbol
	for a value by a line such as:

		s 20 space

	Code which uses this value, such as:

		mov	a,#20h




								Page 11


	will then be disassembled as:

		mov	a,#space

	Labels and symbols differ in that a label applies to an address,
	whereas a symbol applies to any 8 or 16 bit data. For code which
	can only refer to values, such as

		mov	a,#20h

	only the symbol table will be searched for a matching value. For
	code which could refer to either an address or a value, such as:

		mov	dptr,#1234h

	the label table will be searched first, and only if no matching
	value is found will the symbol table then be searched. Symbols,
	like labels, are limited to six characters.

    T DIRECTIVE (text [ascii] data):

	Forces the data in the range specified to be disassembled as
	text (ascii data). Thus the code: 48 69 20 74 68 65 72 65 at
	address 1000H will be disassembled as:

		db	'Hi there'

	or

		ascii	'Hi there'	(command line option A used)

	by putting the line:

		t 1000-1007

	in the control file. Otherwise it would be interpreted as:

		orl	a,r0		; 1000   48	     H
		xrl	a,r1		; 1001   69	     i
		jb	2eh.4,X106d	; 1002   20 74 68    th
		xrl	a,72h		; 1005   65 72      er
		xrl	a,t3		; 1007   65 ff      e.

	which is unlikely to be what was intended by the original
	programmer. Data specified by this directive is not checked
	to verify that it really is ascii data--be careful.




								Page 12


    W DIRECTIVE (word binary data):


	Specifies that the data is to be interpreted as 16 bit binary
	data. For example:

		w 1000-1007

	tells D51 that the data from address 1000H to 1007H should
	generate the lines:

		dw	0
		dw	1
		dw	2
		dw	3

	assuming that the data at address 1000H and up is 00H, 00H,
	00H, 01H, 00H, 02H, etc. This differs from the A (address)
	directive in that the A directive also causes a reference
	to be made to the indirect address. In other words, if the
	data at address 1000H is 1234H, the A directive will cause
	a label (X1234) to be put in the output file at address
	1234H, whereas the W directive will not.




								Page 13


                        FORMAT OF OUTPUT FILE


    The output file (extention .d51) contains 8051 instructions and
    pseudo ops in a format that should be acceptable to any 8051
    cross assembler. When assembled, the source file should produce
    an Intel hex file or binary file that is identical to the original.
    Identical, in this case, means that the code is the same, not that
    it necessarily has the same format. The number of bytes in each
    line of the hex file may differ from the original depending on
    whether the original was produced by an assembler or was read from
    an eprom.

    Each output line is in the following format:

	LABEL:	OPCODE	OPERANDS	; COMMENT

    The label field will be generated only if the address of the code
    is referenced by some other code (a call, for instance), or if the
    user has specified a label for that address in the control file.
    The comment field is only generated if the user specifies the D
    option on the command line. It begins with a semicolon and is
    followed by the hexadecimal address of the instruction, the hex
    value of the byte(s) for the instruction, and finally by the ascii
    representation of the instruction byte(s). For example:

	X004f:	orl	p3,#0ffh	; 004f   43 b0 ff   C0.

	label	opcode	operands	comment

    Several things should be noted in this example. The label is 'X'
    followed by the address of the instruction in four hex digits.
    This type of label is created by D51 when some other code refer-
    ences the address. If the user specifies a label name for the
    address in the control file ('what' for example), the generated
    code becomes:

	what:	orl	p3,#0ffh	; 004f   43 b0 ff   C0.

    If the user were to specify the symbol 'ones' for the value 0ffH,
    the output would then become:

	what:	orl	p3,#ones	; 004f   43 b0 ff   C0.

    Also note the ascii representation of the instruction bytes. Bit
    7 is forced to zero so that ascii with the high bit set can be
    viewed (b0H in the example becomes 30H, which is ascii '0'). Any
    code which is not printable ascii (a control code, for example)
    is output as a period. This is the case for the byte 0ffH above.




								Page 14


    The comment field starts at a different position in the output
    line depending on the type of data in the input file. For normal
    executable code, the comment field starts in column 32; for hex
    data it starts at column 49, and for ascii data it starts in
    column 56. For many programs, this makes for a more readable
    source file, but if there is a mix of data types in a short range
    of addresses, this can lead to some strange looking formatting.
    The user may want to correct this with a text editor in the final
    disassembly before modification and reassembly.




								Page 15


                            BACKGROUND

 
    A disassembler is a program that reads machine code from a binary
    or hexadecimal file and generates an assembly language source code
    file. You may want to do this to recover source code which has been
    lost, or to modify the code in equipment which uses an 8051 processor
    or just for the educational value of finding out how something works.
    The source file generated by the disassembler should be compatible
    with a cross assembler that could then be used to create 8051 machine
    code identical with the original (except for modifications the user
    may wish to make).

    D51 reads the entire 8051/8052 program from the hex or binary file into
    memory, then reads the control file to flag any data the user specifies
    as something other than executable code. When this is done, D51 scans
    the data array containing the 8051 code three times. On the first pass,
    it looks for code such as calls or jumps that reference other code in
    the array. When such code is found, the referenced address is flagged
    so that a label can be output to the source file in the second pass.
    The second pass creates the output file (extention .d51) and writes
    the assembly source code lines. See the section titled 'Technical Info'
    for a description of this process. The third pass through the code
    generates equate statements at the end of the file for anything that
    requires it. This includes labels and symbols defined in the control
    file, addresses that were referenced but are not the first byte of an
    instruction or are not within the program space read from the input
    file, and miscellaneous data values for which no symbol or label has
    been specified in the control file.

    On the first attempt to disassemble your code, use the generic control
    file GENERIC.CTL by copying it to CODE.CTL (where CODE is the name of
    the binary or hex file to be disassembled). After examining the source
    code generated by D51, modify the control file with any ascii text
    editor to force D51 to interpret such areas as executable code (or
    tables of addresses or whatever). Then re-run D51 for a more complete
    disassembly. Repeat this process as many times as necessary to achieve
    an acceptable level of disassembly (please see the documentation for
    control file directives).




								Page 16

                           TECHNICAL INFO

  D51 Disassembly Techniques:

    D51 is a table driven disassembler. The value of each 8 bit opcode to
    be disassembled is used as an index into two tables. The mnemonic table
    ('mnemtbl' in the file D51.TBL) contains ascii text entries for the
    mnemonic for each opcode. The option table ('opttbl') contains 8 bit
    flags which tell D51 what type of opcode is being disassembled so that
    it can generate proper operands.

    D51 first analyzes the command line to get the name of the file to be
    disassembled and any command line options. After finding and opening
    the file, the program allocates two 64K arrays: one to hold the program
    to be disassembled and one for disassembly control flags. Both arrays
    are initialized with codes that indicate invalid data. The input file
    is then read and the data stored in the program array. As the data is
    stored, the corresponding byte in the control array is set to indicate
    valid program data.

    Once the program is in memory, D51 looks for a control file with the
    same name as the program file (but with an extension of .ctl). If a
    control file is found, it is read and the information is used to modify
    the control array flags to indicate what type of data is in the area
    of memory specified in the control file directives. The control file
    can also specify label and symbol names, among other things.

    D51 then executes three passes over the program data. The first pass
    looks for executable code that references some other address (calls
    and jumps, for example.) The referenced address is then flagged (in
    the control flag array) so that a label will be generated in the
    output file during the second pass.

    The second pass does the real work of the disassembler. Pass 2 scans
    the program array and checks to see if the current location contains
    executable code or some other type of data (as specified by the
    control array flags.) If the current location contains some type of
    data that is not executable code, the control flags determine what
    action will be taken. If the control flags specify binary byte or
    ascii data, the data is temporarily stored in a buffer so that multiple
    bytes can be output on one line, rather than having a separate line with
    a DB pseudo op for each byte of data. Word and address data, however,
    do generate a separate line for each entry.

    If the current location contains executable code, D51 outputs the
    mnemonic for the instruction (by using the opcode as an index into
    the mnemonic table), and then uses the option table flags indexed by
    the opcode to determine how to generate appropriate operands. During
    this pass, D51 keeps track of any direct accesses to registers and
    outputs equates for their names at the end of the pass.

    The third and last pass does some clean up work--searching the array
    for references to un-initialized data or references to addresses not
    at the beginning of multi-byte opcodes so that equate statements can
    be generated. This pass also outputs equate statements for the entries
    in the symbol table.



								Page 17


  D51 Source Code:

    The source code for D51 is contained in five files:

	D51.H		Header file defining constants, program flag
			values and data structures.

	D51.TBL		Tables for 8051 mnemonics, SFR names, SFR bit
			names, register names and option flags.

	D51.C		Main function that analyzes the command line,
			finds and opens the disassembly file, allocates
			memory for data arrays and calls the disassembly
			functions in d51p1.c and d51p2.c.

	D51P1.C		Contains 'pass0', which is not really a pass but
			reads the control file and modifies the flag array
			accordingly, and 'pass1' which searches for
			address references. This file also has routines
			relating to the label and symbol tables.

	D51P2.C		Main disassembly routine that generates the output
			file (pass 2). Also contains 'pass3' which generates
			equates for unresolved references and for the
			symbol table entries.

    Each of the C files contains prototypes for the routines in the file.
    If your compiler doesn't support prototypes, it's time to get a new
    compiler.

    The header file (D51.H) defines constants for exit codes, program flags
    and various limits. It also contains structure definitions for symbol
    and label table entries, mnemonic table entries and sfr names. The file
    D51.TBL contains the mnemonic table, the option flag table, sfr name and
    bit name tables and the register name table.

    D51.C is the main disassembler file. The function main() parses the
    command line for user options. It then attempts to open the input file
    (bin or hex) and allocates memory for program and flag data. The input
    file is then read into the program data array.  Main then calls various
    routines in other files to perform the disassembly. D51.C also has the
    following routines:

	atox()		Converts ascii hex to binary hex data.
	getcode()	Extracts data from ascii hex file and puts it in
			the 64K program array.
	find_entry()	Searches for an entry in the symbol or label table.
	get_smem()	Allocates memory for a new symbol or label entry
			and links it into a doubly linked list.
	add_entry()	Adds a new entry into the symbol or label list.

    D51P1.C contains pass0(), which isn't really a disassembly pass, but
    reads the control file (if any) and sets up the program flag array




								Page 18



    according to the directives found in the control file. The label and
    symbol tables are built from data found in the control file. Pass1()
    scans through the program array and, if the program flags define the
    data as executable code, determines if the code references a program
    location (jumps, calls, etc). Any such references set the program
    flags for the referenced address. This is necessary so that pass 2 can
    generate labels for the referenced addresses. D51P1.C also has routines
    to dump accumulated data for db pseudo ops (ascii and binary).

    D51P2.C is the real workhorse of the disassembler. Pass2() generates
    the output assembly source file by scanning through the program array
    and disassembling the code based on the program flag array info. If
    the program flag specifies that the data is code, the opcode byte is
    used as an index into two arrays: the mnemonic table, which contains
    ascii text for the opcode, and the option table, which has bit flags
    to tell D51 what type of operands are involved. It is this table
    driven feature that makes D51 a fast disassembler. This technique,
    however, limits any disassembler based on it to processors that have,
    at most, 64K of program space. It would not be applicable to, for
    example, a 680x0 processor, which can have up to 4 Gbytes of program
    space (unless you have a computer that can handle 4 Gbyte arrays). If
    the program flags specify that the data is ascii or binary data, the
    data is saved in a separate array so that many bytes can be output
    with one db pseudo op. When pass 2 is complete, pass3() rescans the
    data array looking for references that require equate pseudo ops. Pass
    3 also outputs equates for symbol and label table entries.

    Further details of D51's implementation can be found by examing the
    source files.




								Page 19


                              SUMMARY


    D51 V2 is being distributed under the GNU General Public License.
    Complete source code for D51 MUST accompany any distribution of this
    software. You are free to modify it in any way you see fit, but you
    are NOT free to market it as a commercial product (except for reason-
    able fees for media or other reproduction and/or distribution costs).
    See the file COPYING for details.

    D51 V2 is an 8051/8052 disassembler that allows the user to specify
    how code should be disassembled via a control file that defines given
    areas of the code as ascii text, binary data or other types of non-
    executable code. By an iterative process of disassembly, control file
    modification, and further disassembly, the user can obtain a very
    readable source file that can then be modified and re-assembled by an
    8051 cross assembler. Several public domain 8051 cross assemblers are
    available.

    I've encountered several problems when reassembling the output of D51.
    Almost all are due to the cross assembler not recognizing SFRs of some
    of the newer or more exotic 8051 variants. The D51 tables include
    names for all SFRs that I'm aware of as of May 1995 (there are likely
    some that I'm not aware of). Such errors might be corrected just by
    defining a symbol for the SFR in the control file (see the F directive),
    but this depends on whether your cross assembler will accept it as a
    valid operand. If all else fails, replace the offending instruction
    with a 'db' pseudo op and put the mnemonic and operand in a comment.
    A similar problem is the assembler not being able to handle a bit
    addressable SFR address; the only solution I see to this is to use a
    'db' pseudo op. All other problems I've seen (not many) have been due
    to disassembling data as code; this is easily corrected by modifying
    the control file to specify the correct data type.

    D51 V2 was compiled using Borland's Turbo C V2.0 and is intended to
    be run on MSDOS machines. No attempt was made to make it portable to
    either other compilers or other operating systems. The source code for
    D51 should require little or no modification to be compatible with
    other compilers for MSDOS, but may require some significant changes to
    run on other operating systems. The source code was created using
    Borland's Brief V3.1 and may require reformatting for other editors
    (see the file TAB.DOC).




								Page 20


Command line options:
    A - Change db/defb pseudo op to 'ascii' macro for text
    B - Force read of binary file (.bin extention)
    D - Add address and data info in comment field
    H - Force read of Intel hex file (.hex extention)
    S - Change db and dw pseudo ops to defb and defw
    X - Add hexadecimal offset to all program locations

Control file directives:
    A - Specifies that words in program space are addresses
    B - Data is 8 bit binary
    C - Program space is executable code
    F - Specify SFR label
    I - Ignore data (uninitialize program space)
    K - Specify label for SFR bit
    L - Define label
    R - Define register name
    S - Define symbol
    T - Specify ascii text
    W - Data is 16 bit binary




								Page 21

                          8051 REGISTER MAPS

Addresses of 8051 registers:

Register Bank   R0  R1  R2  R3  R4  R5  R6  R7
----------------------------------------------
    0           00  01  02  03  04  05  06  07
    1           08  09  0A  0B  0C  0D  0E  0F
    2           10  11  12  13  14  15  16  17
    3           18  19  1A  1B  1C  1D  1E  1F

Addresses of 8051 Special Function Registers:

Address Symbol Name
----------------------------
   80   P0     Port 0
   81   SP     Stack Pointer
   82   DPL    Data Pointer (low byte)
   83   DPH    Data Pointer (high byte)
   87   PCON   Power Control
   88   TCON   Timer/Counter Control
   89   TMOD   Timer/Counter Mode
   8A   TL0    Timer/Counter 0 (low byte)
   8B   TL1    Timer/Counter 1 (low byte)
   8C   TH0    Timer/Counter 0 (high byte)
   8D   TH1    Timer/Counter 1 (high byte)
   90   P1     Port 1
   98   SCON   Serial Port Control
   99   SBUF   Serial Data Buffer
   A0   P2     Port 2
   A8   IE     Interrupt Enable
   B0   P3     Port 3
   B8   IP     Interrupt Priority
   D0   PSW    Program Status Word
   E0   ACC    Accumulator
   F0   B      B Register




Bit Addressable Special Function Registers:

Address Symbol SFR bit Name
-------------------------------
   80-87       P0.0-7  Port 0 Bits
   88   IT0    TCON.0  External Interrupt 0 Type Control
   89   IE0    TCON.1  External Interrupt 0 Edge Control
   8A   IT1    TCON.2  External Interrupt 1 Type Control
   8B   IE1    TCON.3  External Interrupt 1 Edge Control
   8C   TR0    TCON.4  Timer 0 Run Control
   8D   TF0    TCON.5  Timer 0 Overflow Flag
   8E   TR1    TCON.6  Timer 1 Run Control
   8F   TF1    TCON.7  Timer 1 Overflow Flag
   90-97       P1.0-7  Port 1 Bits
   98   RI     SCON.0  Serial Receive Interrupt Flag
   99   TI     SCON.1  Serial Transmit Interrupt Flag
   9A   RB8    SCON.2  Serial Receive Bit 8
   9B   TB8    SCON.3  Serial Transmit Bit 8
   9C   REN    SCON.4  Serial Receive Enable
   9D   SM2    SCON.5  Serial Port Mode Specifier
   9E   SM1    SCON.6  Serial Port Mode Specifier
   9F   SM0    SCON.7  Serial Port Mode Specifier
   A0-A7       P2.0-7  Port 2 Bits
   A8   EX0    IE.0    Enable External Interrupt 0
   A9   ET0    IE.1    Enable Timer 0 Interrupt
   AA   EX1    IE.2    Enable External Interrupt 1
   AB   ET1    IE.3    Enable Timer 1 Interrupt
   AC   ES     IE.4    Enable Serial Port Interrupt
   AF   EA     IE.7    Enable Interrupts
   B0-B7       P3.0-7  Port 3 Bits
   B8   PX0    IP.0    External Interrupt 0 Priority
   B9   PT0    IP.1    Timer 0 Interrupt Priority
   BA   PX1    IP.2    External Interrupt 1 Priority
   BB   PT1    IP.3    Timer 1 Interrupt Priority
   BC   PS     IP.4    Serial Port Interrupt Priority
   D0   P      PSW.0   Parity
   D2   OV     PSW.2   Overflow Flag
   D3   RS0    PSW.3   Register Bank Select Bit 0
   D4   RS1    PSW.4   Register Bank Select Bit 1
   D5   F0     PSW.5   Flag 0 (general purpose flag)
   D6   AC     PSW.6   Auxiliary Carry Flag
   D7   CY     PSW.7   Carry Flag
   E0-E7       ACC.0-7 Accumulator Bits
   F0-F7       B.0-7   B Register Bits