ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                                      º
             º   S E R I A L   P O R T S   M A N A G E R    v 2.20  º
             º                                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍ(C)opyRight. HETRU 1991-1995ÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                         13, chemin de la croix St Vincent
                           94430 CHENNEVIERES SUR MARNE
                                      FRANCE





      The only communication "protocol" distributed (in assembler, PASCAL,
    and C) is the ASCII <-> HEXADECIMAL transcoding. Its main interest is
    when you decide to use the Xon/Xoff hand-shaking (integrated in the
    serial ports driver), whereas you have to transmit some binary data...
    Otherwise, there could have confusion - to the driver level - between
    data bytes and Xon/Xoff control bytes !
    ATTENTION: To each hexa. bytes transcoded corresponds 2 ASCII bytes.
    The speed of a link based on this transcoding will therefore be
    divided by 2 ! THEREFORE: Use it WITH DISCERNMENT !...
      For the arguments meaning, please refer to the listing associated
    with the indicated procedures.

     ÄÄÄÄÄÄÄÄÄÄÄÄ
       Constants:
     ÄÄÄÄÄÄÄÄÄÄÄÄ
       No constants.

     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Globals variables:
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       No specials variables.

     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Available procedures and functions:
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     ConvAsc et ConvAscii:
       Converts any hax. byte into 2 binaries associated to 2 ASCII characters
       (whose hexa. codes are greater than 29h).
     ConvHex et ConvHexa:
       Converts 2 ASCII BINARIES codes into THE corresponding hexa. code.