MODEM INTERFACING:
 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      The MODEM.PAS library shows how to interface a modem by using the pro-
    cedures offered with SERIAL PORTS MANAGER. You could insert in it some
    other sequences of HAYES commands, or write a special interfacing adapted
    to some other modems NOT HAYES compatibles...

      MODEM.C is the translation of MODEM.PAS in Turbo-C (C).

      For the assembler, it is sufficient to proceed in a similar way.

      A simple demonstration of how to use each of these libraries is distri-
    -buted with SERIAL PORTS MANAGER: TESTMODP.EXE (for MODEM.PAS) and
    TESTMODC.EXE (for MODEM.C).
    !! ATTENTION: modify the "CommPort" variable in these programs before
    !! compiling them, in order to use the serial port on which your modem
    !! is physically installed !

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³Globals variables (PASCAL and C types: PAS/C) ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ModemUsed       SHORTINT/byte      Modem type used: Hayes or Minitel ?
                                     Permit to send the specifics commands
                                     associated to the modem to drive !
                                     Its initial value is 'Hayes'.
                                             MINITEL <---> TlTex
                                             HAYES   <---> Hayes
  DTR_Cmde        BOOLEAN/byte       Using DTR as a command prefix or NOT ?
                                     Default is TRUE. IF this variable is
                                     set to FALSE, the following prefix
                                     MUST be sent first before each command.
  HAYESPrefix     STRING[3]/char[4]  Command prefix for the HAYES modems.
                                     '+++' = default value.
  PulseDial       BOOLEAN/byte       TRUE if you want a pulsed call, FALSE
                                     if you need a frequency call.
                                     Its default value is TRUE.
  connected       BOOLEAN/byte       Informes on the connection status. TRUE
                                     if the line is connected, FALSE if not.
                                     Is up-dated by the clock interrupt
                                     function. FALSE is its intial value.
  Show_CorF       BOOLEAN/byte       Write the connection sign on the screen?
                                     TRUE => The sign is written each second
                                     on the screen when the clock interrupt
                                     procedure is installed.
                                     Default value is FALSE.
  Int1CSave       POINTER/<NIL>      Stores the INT 1Ch vector initial value.
                                     Used to activate or disactivate the clock
                                     interrupt procedure in the PASCAL library.

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³Available procedures (PAS and C):³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  1ø/ To send any command to the modem:
         PROCEDURE CmdeToModem(TypCmde: BYTE;DataCmde: CmdeStr);
         void CmdeToModem(byte TypCmde, char *DataCmde)
             Possible values for 'TypCmde':
               Personal command     <---> Generique
               Initialization       <---> InitMod
               Connection           <---> Connect
               Call a given number  <---> Appel
               Hand-off the line    <---> Raccroch
               Minitel "Connex/Fin" <---> ConnexFin

  2ø/ Clock interrupt made to check the connection status:
         PROCEDURE Check_HModem_State; INTERRUPT;

  3ø/ To have more informations, report yourself to the listing... Specially
      in C, the 2 following procedures permit to install/uninstall the clock
      interrupt made to check the connection status...
         void install_Clock(byte com)
         void un_install_Clock()