ÉÍÍ SERIAL  PORTS  MANAGER   version 2.20 ÍÍ»
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


                           TECHNICAL FEATURES OF THE
                          SERIAL PORTS MANAGER PACKAGE
                    UNDER MS - D O S and COMPATIBLE SYSTEMS



      þ Installation and setup made easy (SETPILOT.EXE utility and INSTALL.BAT,
      a DOS batch file).


      þ Able to detect the used material: type of computer, types of the
      available UARTs, and IRQ that are associated to them.


      þ Fully benefit from the speedy 16550 UART (with its internals buffers).


      þ Possible simultaneous management of up to 8 serial ports; the IRQ
      2,3,4,5,7,10,11,12 and 15 are all usable, and the addresses of the
      serial ports may fully be set as needed. The communication driver
      could search by itself the IRQ lines physically associated to every
      available port on the used machine (provided that no conflicts
      exists in their physical assignments !).


      þ Offers serial communications with buffers and flow management
      (software and/or hardware hand-shaking of any possible type...).


      þ Is able to manage several UART to the means of one same interrupt
      line (it is necessary and sufficient that your hardware supports that !)


      þ Enhances the serial communications BIOS part (INT 14h) with all the
      functions exposed above !


      þ Offers a complete control on the initializations and the internal
      working of the driver to the means of SETPORT.COM, an external utility
      that could be used at any time: your serial ports then become fully
      mastered from your DOS prompt, at your finger-tip...


      þ May as well be used as a simple BIOS layer, or as a DEVICE DRIVER
      integrated to the operating system, or as a programming library
      to be included to yours developed programs (by using SCLIB.OBJ...).


      þ The interfacings for the C and The PASCAL are fully distributed (in
      standard) with their sources, and with a few demonstrations !



                                                  HETRU Fabrice
                                         13, Chemin de la croix St Vincent
                                            94430 CHENNEVIERES sur MARNE
                                                     FRANCE