S E R I A L     P O R T S     M A N A G E R     v 2.20
              ------------------------------------------------------
                S.T.A.R.COMM     Serial Turbo Async. Resident COMMs
              ------------------------------------------------------
                                                            10/20/95

              ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ(C)opyRight HETRU 1991-1995ÍÍÍÍÍÍÍÍÍÍÍÍÍ
                         13, chemin de la croix St Vincent
                           94430 CHENNEVIERES SUR MARNE
                                      FRANCE
                             tel: (16-1) 45-93-27-38

                         CompuServe address: 100414,1524
                       Internet: 100414.1524@Compuserve.com




                             U S E R    G U I D E





           REMARK: In all this document, STARCOMM.EXE could be replaced by
       STARCOM8.EXE. STARCOMM.EXE is interfacing no more than 4 ports, whereas
       STARCOM8.EXE could support up to 8 ports ! (All the values limits
       specified in the following text are for STARCOM8: we refer to "COM8:"
       or to "8" ports or buffers. Just change these values to "COM4": or "4"
       if you consider STARCOMM !)





                             TABLE OF CONTENTS





   Introduction........................................................ 1



   I- Functional features of STARCOMM.................................. 2



   II- Respective advantages between "BIOS" and "DEVICE DRIVER" installations

       1- Used in the BIOS (T.S.R.) mode............................... 4

       2- Used in the DEVICE DRIVER mode............................... 4

       3- When using the library (SCLIB.OBJ)........................... 4



   III- STARCOMM.EXE COMMAND SYNTAX

       1- To load the driver in its T.S.R. BIOS mode................... 5

       2- To load the driver in its DOS DEVICE DRIVER mode............. 5

       3- Commands and options known by STARCOMM.EXE................... 6



   IV- USING SPECIFIC(S) DEVICE(S) ON SERIAL PORT(S)

       1- Using a mouse in 'competition' with STARCOMM................. 13

       2- Accessing to an internal or external modem................... 13

       3- All type of devices knowing a protocol....................... 13



   V- SETPORT.COM UTILITY

       1- Syntax of SETPORT.COM........................................ 14

       2- Command options of SETPORT.COM............................... 14



   ANNEX A:  Principle of the null-modem cable......................... 17

   ANNEX B:  Types of UART chips on PC and compatibles................. 19

   ANNEX C:  Why a "BIOS emulation" ?.................................. 20

   ANNEX D:  Files making SERIAL PORTS MANAGER v2.20................... 21


                                                                        1





                               INTRODUCTION









      This document exposes the main features of the serial driver, and the
    different ways STARCOMM.EXE can be used.

      This driver was developed in 8086 assembler language on IBM-PC and works
    under MS-PC/DOS and all compatibles operating systems (DR-DOS, DOS "task-
    windows" under WINDOWS and OS/2, etc.).

      The SETPORT.COM utility allows to modify the mode of working and the
    initialization of STARCOMM by nominative port, as well as visualizing the
    states of all the serial ports recognized by this driver (when found
    resident in memory...). It also presents the advantage, over the
    command-line interfacing offered by STARCOMM.EXE, that it doesn't
    reactivate the default values of the different driver parameters.

      The TESTSTAR.EXE demonstration (source *.PAS) permits to visualize
    the efficient working of STARCOMM, and permits to test locals serial links
    (TESTSTAR is a multi-ports processus).
      The TERMINAL.COM program (developed in C) demonstrates the utilization
    of STARCOMM when loaded in its DEVICE DRIVER mode. It creates a communica-
    -tion active on one channel at a time (it is a simple TTY emulator...).

      The REMOTE.EXE utility allows you to exploit a second IBM computer
    from a computer called "local". The "local" IBM then acts like the normal
    console of the distant IBM (called the "REMOTE" !). It is a small
    application gracefully offered with SERIAL PORTS MANAGER in order to give
    an example of what this package can do for you.

      The "EXISTENCE" of a port answers to the double following condition:
    the address that it wants to use correspond to a physically present UART,
    AND the IRQ it is assigned to could be installed (ATTENTION: if an other
    program comes to reroute this IRQ after the installation of STARCOMM, the
    port will be un-usefull to establish any serial link to the means of
    STARCOMM whereas the port will always remain "EXISTING", and this until
    restitution of our vector by this other application...).
      A port is said "OPENED" when the electric logical signals of the PC
    are set in order to activate the interrupts that are physically going
    to allow a completely functional link. Otherwise, this port will be
    said "CLOSED" !


                                                                        2


  I  - Functional features of STARCOMM:
  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
    þ STARCOMM.EXE could be loaded from the DOS prompt (like any standard
  program) or from the CONFIG.SYS (DEVICE=STARCOMM.EXE...).

    þ In order to get an information page and a brief help, use the "?"
  character (the "/" character is not compulsory):
                          x> STARCOMM /?

    þ ErrorLevel codes returned by the installation module in BIOS mode:
          0 --> No error: requested action correctly done,
          1 --> End of program on impossibility to un-install.

    þ This driver manages, under hardware interrupt(s), the serial ports COM1:
  to COM8: of compatible PC/AT in using buffers in RAM memory. There are
  1 receipt buffer AND 1 transmit buffer for each port recognized at the
  installation time (except orders making a more explicit limitation in the
  command-line). The receipt buffer is 1 kilo-byte in size, whereas the
  transmit buffer is reduced to 1/2 kilo-byte by default. It is possible to
  fix each buffer size between « and 55 kilo-bytes. It is also possible,
  for each application, to define its own buffers of any sizes in the limit
  of ONE segment (of the CONVENTIONAL MEMORY) for each serial port used:
  every acknowledged port can thus dispose of up to 64 Kilo-byte of I/O
  buffers if needed !

    þ STARCOMM manages asynchronous communication ports in exploiting the
  availables UART on the IBM. These UART could be a 8250, 16450 or 16550
  type. If an 16550 UART is available on a given serial port, its FIFO mode
  is automatically exploited (excepted if forbidden from the command-line !).

    þ The Request_To_Send(RTS)/Clear_To_Send(CTS) and Data_Terminal_Ready
  (DTR)/Data_Set_Ready(DSR) signals can be managed by the STARCOMM communi-
  cation processes, as well as RI, DCD and OUT1 ! The software hand-shaking
  Xon/Xoff is also acknowledged, and can be activated and dis activated, as
  can be RTS/CTS and DTR/DSR. This can be ordered from the DOS prompt, or
  using the software interrupt giving access to the serial driver functions
  (Int 14h). The hexa. codes to use for Xon and Xoff can be define as needed.

    þ All group of 10 consecutives received errors provokes a complete
  initialization of the controller associated to the serial port used, this to
  avoid any possible interference with any other programs reaching the port
  in the local machine. To this effect also, the BIOS software interrupt 14h
  is filtered by STARCOMM (case of the programs using the serial ports via the
  BIOS: in this case,they provoke a communication format resetting to the level
  of our driver). As a consequence, for example, this implies that any
  initialization made using the DOS "MODE" utility will be acknowledged by the
  STARCOMM driver...
  Remarks:     1- Any initialization request on an inhibited port (Cf. III-3)
     will be rejected by our filtering of the BIOS interrupt 14h.
               2- The BIOS variables addressing the UART chips are up-dated by
     the driver. They are reseted in their initial state at the time of the
     STARCOMM uninstallation.
               3- The time-out BIOS variables are not, in any case, altered
     by STARCOMM.


                                                                        3



    þ STARCOMM filters the basics interrupt 14H BIOS functions: it redirects
  to the driver any commands sent to an open serial port. From then on, it
  is the addresses and all the technical features of STARCOMM that are stakes
  to disposition of ALL the DOS comm. applications based on the BIOS level.
  These applications will therefore have their performances distinctly
  improved, and they will be able to gain the mapping benefit offered by
  STARCOMM.EXE (see "/A..." and "/I..." options...).
    Example: suppose D_COMM.EXE only uses the COM1 (via the BIOS), and your
  modem is installed as a COM3:, using the IRQ 7.
           execute:
                   x> STARCOMM /A1=03E8 /I1=7
                   x> SETPORT COM1: /O /Inform
           ...and then:
                   x> D_COMM              And that's all !...
    REM: Thanks to the "/EB" option that activate the STARCOMM BIOS emulator,
  it could be avoided having to open the port to use (Cf. ANNEX C) !
  However, no buffer will be used by the driver in this last case.

    þ ATTENTION: After the installation and/or after any parameter(s)
  modification from the driver command-line, the ports are reseted in their
  UNACTIVE state (except using option "/O..."). Any application wanting to use
  port(s) in order to communicate will therefore have to initially take
  carefulness of reopening the appropriate(s) port(s)...

    þ STARCOMM can generate 2 kinds of transmitting: a slow transmission (18
  bytes by seconds), and a fast transmission (continuous flow only limited by
  the capacity of the UART to transcode the bytes). On 8 simultaneous opened
  ports, each one could dispose of its own transmitting mode. The choice of
  the mode to activate only depends on the device with which it is necessary
  to converse. For example, to make a direct local link with a Minitel, it IS
  necessary to activate the slow transmission because this terminal doesn't
  presumably work in an interrupt way: if too much bytes arrives between 2
  Minitel scans, there is overrun, and therefore loss of information to the
  Minitel level. In general, for all device working in a scanning mode, it is
  necessary to activate the slow transmission of STARCOMM (thus creating an
  everage transmission of 18 bytes a second...).

    þ IMPORTANT REMARK ON HARDWARE INTERRUPTS SHARING:
  Only the specials multi-serial ports cards and the IBM-PS/2 computers
  permits several serial ports to share a same IRQ. If you joined several
  ports on a same IRQ with any other material (PC, XT or AT), know that you
  must NOT open at the same time all these ports. It will then be necessary to
  always open only ONE of these ports at a time for it to be fully working !
    (! THIS IS A HARDWARE LIMITATION NOT SURPASSABLE BY ANY SOFTWARE !)


                                                                        4



  II- Respective advantages BETWEEN "BIOS" and "DEVICE DRIVER" installations
  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      1- Used in the BIOS (T.S.R.) mode:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      þ Uses less RAM memory (the DOS normalized interface doesn't remain
      in RAM memory after the driver installation !).
      þ Ability to un-install the driver when becoming useless in RAM, without
      having to fully reset the computer;
      þ Complete relative independence to the operating system, so that:
        . considerable increase on execution speed of the services offered
          by the driver: indeed, the DOS layer being absent in the case of an
          Int 14h, every logical access to the driver corresponds to an unique
          physical call to this driver (where a DOS interface function could
          easily achieve it by at least 4 DOS internals calls !),
        . and absence of any trouble on EOF code (^Z) management that is merely
          unknown to the interrupt 14h.



      2- Used in the DEVICE DRIVER mode:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

        The driver is here-by known by the DOS. It opens the access to a new
      logical device (referred as "COMM:" by default) to which it is possible
      to access with no more programming using the DOS shell (COPY CON: COMM:)
      OR, with programming, using any computer language (use the DOS standard
      files access functions integrated to all programming languages !).



      3- When using the library (SCLIB.OBJ):
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

        This serial port driver format is not usable from the DOS prompt.
      It is only usable by the programers in order to integrate the kernel
      of SERIAL PORTS MANAGER directly to their creations,this to avoid any de-
      -pendence between their programs and any external driver if he wants to !
        The application thus developed will only benefit the BIOS mode, with
      the advantages associated (report to part 1-...) PLUS the advantage to
      be able to call the driver services without transitting through the
      interrupt 14h (Cf. STAR-REF.DOC on this...).
        The ability, for each application, to define its own external buffers
      for each serial port negates the fact that the library only integrates
      2 very small buffers for each port by default (1/2 kilo-byte each...).


                                                                        5



  III- STARCOMM.EXE COMMAND SYNTAX
  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
      STARCOMM.EXE can be loaded as an external driver to the DOS (in its
  "BIOS" mode) OR as a DEVICE DRIVER (thus creating a "character" type file
  named "COMM:" by default).
      The SETPILOT.EXE utility can help you to get in touch with the
  numerous options that STARCOMM.EXE knows !



      1- To load the driver in its T.S.R. BIOS mode:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      From the DOS command line (the "prompt"...), just order:
d>[<drive>:][<\path\>]STARCOMM [COM:][speed][,parity][,bits][/<options>]
      The only software interrupt to access the STARCOMM services will
  then be the interruption number 14h.



      2- To load the driver in its DOS DEVICE DRIVER mode:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Integrate the following order in your CONFIG.SYS:
   DEVICE=[<drive>:][<\path\>] STARCOMM
                    [COMi:][speed][,parity][,bits][/<options>]
      In addition to the interrupt 14h, STARCOMM will thus be also
  accessible by using the DOS interrupt 21h FILES functions;
  and you will even have access to the "COMM:" file at any moment
  from the DOS prompt.


                                                                        6



      3- Commands and options known by STARCOMM.EXE:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      The initialization format explained below takes effect for
    the whole acknowledged serial ports of the driver.

        [COM:]    = Announces the definition of the format initializations.
                    When STARCOMM has been (or is) loaded as a
                    DEVICE DRIVER, specifying COM1: (or COM2:, etc...) allow
                    to orientate the logical file ("COMM:" by default) on the
                    serial port thus specified.
        [speed]   = {110,150,300,600,1200,2400,4800,9600,19200,28800,38400,
                    57600, or 115200} bits a second (9600 by default).
        [,parity] = {N, P, I, T, or R} for 'N' no, 'P' even, 'I' odd,
                    'T' work, or 'R' rest (N by default).
        [,bits]   = {5,6,7 or 8} for a coding on 5,6,7 or 8 bits (8 default).
        [,stop]   = {1 or 2} for 1 or 2 stop-bit(s) (1 by default).

      The working-control options recognized by STARCOMM are:

        [/A<N>=<address>[,<N>=<address>[,...]] =
                    Use <address> (in hexa.) for the port <N>, then... For
                    each specification, give the address of the first associate
                    UART register for the indicated port number. At this
                    address, if no UART is detected, the associate port will
                    not be functional and treated as INEXISTANT by the driver.
                    Every specified address must be made of 4 numbers: write
                    /A3=0370 and not /A3=370 !...
                    Note that in permuting some addresses between different
                    existing ports, you could redirect the standard DOS ports
                    (attention to the IRQ linkage !...).
                    ATTENTION: This option is unknown for the ports of which
                    the IRQ seems to be rerouted by a program loaded after
                    STARCOMM.EXE (in order to respect the consistency of the
                    IRQ chain in the computer !).
        [/I<N>=<num>[,...]] = Use the <I>RQ number <num> for COM<N>:.
                    Only the IRQ 2, 3, 4, 5, 7, 10, 11, 12 and 15 are admitted.
                    Any indicating sequence can be used with no importance. The
                    erroneous or forbidden indications will be unknown. If a
                    program installed after STARCOMM.EXE has rerouted some
                    interrupts used by STARCOMM, it won't be possible to modify
                    these IRQ for the associated port(s), and this until
                    un-installation of that post-loaded program. The Order is
                    then unknown (no apparition of new IRQ number in the driver
                    message !). In case of repetitions for a same port, only
                    the last specification will be considered as consistant.
                    REM: Don't use IRQ2 on AT and PS/2, this IRQ being
                         reserved to a second 8259 (interrupt controller)
                         installed in cascade on these machines ! Don't use
                         IRQ5 on the XT machines (providing hard disks). At the
                         time of the installation (as well as at the time of
                         any parameters modifications), a demand for IRQ2
                         on an AT or a PS/2 or a demand for IRQ5 on an XT will
                         be rejected. The IRQ10 and above could not be accepted
                         on AT or PS/2 equivalents !


                                                                        7



        [/G<num>[,<num>...]] = I<G>nore the serial ports <num>. Permit
                    the cohabitation of STARCOMM with other drivers working on
                    serial port(s) too (we can explicitly dedicate them one
                    or several ports: report to the paragraph IV about
                    this topic...). This option also permits to manage the
                    conflictual problem of sharing hardware interrupts on the
                    materials that don't support these sharings (ex: if you
                    have a COM2: and a COM4: both linked to the IRQ3 on an AT,
                    forbid either before executing TESTSTAR.EXE; because this
                    program opens all the marked present ports, it would result
                    of it, in the contrary case, a conflict that would block
                    either port COM2: or COM4:, in truth the two !...).
                    Forbidding the access to all the ports won't forbid to load
                    STARCOMM.EXE; but there won't be any possible communication
                    in this case (except utilization of the function 0Ah of the
                    services interrupt 14h...) !
                    ATTENTION: This option is never USEFUL when used to
                    modify an already RAM-installed STARCOMM setup whereas it
                    tries to act on a port of which the interrupt seems to be
                    redirected by an other application than STARCOMM ! Allowing
                    such a maneuver would set the logical existance statutes of
                    the serial ports unconsistant with the real state of the
                    machine's vectors diverted by the asynchronous ports
                    driver; and then, some declared "EXISTING" ports could
                    not be functional. Besides, it would become impossible to
                    uninstall STARCOMM.EXE, even after all competitor
                    applications (to the level of the used interrupts...) have
                    been themselves uninstalled !
        [/V<nø>[,<nø>,...]] = Locks the speed for the specified comm ports.
                    Any new speed would be substituted by the locked one !
        [/F<nø>[,<nø>,...]] = Locks the comm <F>ormat. Same as "/S"...
        [/EL<num>[,<num>...]] = s<E>nd s<L>ow on the port <num>. Permit
                    to activate the transmission in its reduced flow for the
                    specified ports. It will be the clock interrupt (and not
                    the UART one) that will order them to send out some bytes
                    contained in the transmit buffers of the specified ports.
                    It will therefore be 18 bytes a second (maximum...) that
                    will be transmitted toward the outside.
        [/O<num>[,<num>...]] = <O>pen the serial ports <num> as soon as
                    the installation is finished. Using the device attached to
                    "COM<num>:" is then possible as soon as the driver is
                    installed.
        [/EB]       <E>mulator <B>IOS permit not to redirect the calls of the
                    interrupt functions 1 to 5 toward the original BIOS int.
                    14h. A BIOS emulation code is then activated. It presents
                    the advantage of using the addresses, the time-out values,
                    and the respect of the hardware hand-shaking signals that
                    are all imposed to the STARCOMM driver. This code executes
                    its inputs/outputs directly on the physical specified
                    port (buffers are not used...).


                                                                        8



      Each of the following options take value for all the ports known as
    existant by the installed driver. In order to act only on one port, it is
    necessary to act in using the software interrupt of the driver interface
    (this results of the will to preserve the driver installation process
    from being too complex; use SETPORT.COM in order to control the ports
    separately from one another...).

        [/PC]     = Knows the used machine as a <PC>. The IRQ2, 3, 4, 5 and 7
                    will be all authorized for utilization. This command is to
                    reserve for the old computers (BIOS of 1985 and before
                    generally) or for those that declares of erroneous way
                    (compatible PC to the BIOS little compatible (!), or
                    advanced machine "under-configured": ex. an XT without
                    hard disk --> its IRQ5 is therefore free !...).
        [/XT]     = Knows the used machine as an <XT>. The IRQ2, 3, 4 and 7
                    will be the only IRQ authorized.
        [/AT]     = Knows the used machine as an <AT>. The IRQ3, 4, 5, 7, 10,
                    11, 12 and 15 will be the only authorized.
        [/PF]     = Leave <P>orts <F>IFOs un-activated on the found 16550.
                    This option surpasses the following one.
        [/F=<Nb. of bytes>] = Number of bytes of the 16550 UART buffers to use
                    at the transmit process level. "<Nb. of bytes>" must be
                    included between 2 and 15, otherwise the option is merely
                    unknown, and the default value of 14 is then used.
                    REMARKS: Indeed,16 bytes do constitute this physical buffer
                    of the 16550 UART. STARCOMM only allows a maximum of 15
                    because it seems that some kinds of these UART loses
                    some informations if the software tries to benefit from the
                    transmit buffer in its entirety !
                      In receipt, the FIFO is always exploited on 14 bytes
                    (the "trigger level" is frozen to 14 by STARCOMM). It is
                    the maximal value authorized by the hardware !
        [/AI]     = <A>utoscan <I>RQ... The driver automatically research on
                    which IRQ lines are installed the serial ports found at the
                    specified addresses. The "/I=..." option has priority on
                    this "/AI" option that can reveal itself not reliable on
                    some hardware (particular modems OR very fast computers...)
                    NEVER USE OPTION "/AI" UNDER WINDOWS OR THE OPERATING
                    SYSTEM WILL CRASH ! ! ! .
        [/S[=<hexa_code>]] = Activate the <S>ubstitution process of the bytes
                    specified as deficient upon receipt by the specified code.
                    This code could be specified in the room of term
                    <hexa_code>. The default value used is 0FEh.
                    /S=NULL (or "/S=N" because only the first letter of
                    "Null" is really necessary !) permit to order the
                    voluntary loss of any erroneous byte received.
        [/K[=<code_hexa>]] = Activate the function of representing, in the
                    receive buffers, the received BREAKs. <code_hexa> is the
                    code that will represents the BREAKs. /K without any more
                    specification will force the use of 03h to represent a
                    BREAK in the buffer. /K=Null stops this function.


                                                                        9



        [/<nb>] = Permits to limit the number of buffers pairs (transmit/
                    receive) that the driver could open in RAM. By default,
                    STARCOMM reserves 1 pair of buffers by port physically
                    acknowledged during the installation process.
                    Attention: limiting the number of buffers pairs also
                    limits the number of serial ports that it will be possible
                    to open at the same time ! <nb> is limited between 1 (at
                    least 1 buffer to create !) and 8 (i.e. the biggest
                    possible number of usable ports). This option could only
                    be acknowledged by the installation process of STARCOMM.
                    Otherwise, it is ignored, and the correspondent message
                    displayed will only be a recall of the number of buffers
                    the driver knows it can create in RAM.
                    REMARK: In order to save room in memory, it is better
                    to load "STARCOMM/1" when it is going to be used with
                    mono-link applications (some emulators generally...),
                    whereas several serial ports exists on the used machine.
        [/BR=<size>] = Specification of the memory size to allocate to the
                    <R>eceipt <B>uffer(s). <size> must be included between
                    « and 55 Ko., and won't be acknowledged but at the time
                    of the first installation of driver in memory. Thereafter,
                    the driver will satisfy of recalling the buffers used
                    due to the initial installation. In order to modify
                    the size of the receive buffers, uninstall then install
                    again the driver with a new <size> value !
        [/BE=<size>] = Specification of the memory size to allocate to the
                    s<E>nd <B>uffer(s). The notes on the reach of this option
                    are identicals to those of the option above. NOTE that if
                    the added sizes of all the buffers to create passes the re-
                    maining free room in the driver segment, the sizes of these
                    buffers will be automatically reduced in order to contain
                    the buffers in the limit of this segment ! The sizes
                    finally restrained will always be a multiple of 1024 bytes.
        [/R=<tps>] = Definition of the time limit to the tip of which the
                    impossibility of <R>eceiving must abort on a time-out
                    error... The <tps> parameter, that must be included
                    between 1 and 255, explicit the maximum number of half a
                    second to wait before generation of a receiving time-out.
        [/E=<tps>] = Definition of the time limit to the tip of which the
                    impossibility of s<E>nding must abort on a time-out
                    error... The <tps> parameter, that must be included
                    between 1 and 255, explicit the maximum number of half a
                    second to wait before generation of a transmitting
                    time-out.
        [/LC]     = "<L>ocal <C>lear_to_send": The local site must recognize
                    the RTS/CTS hand-shaking: it checks CTS=TRUE before any
                    send, but it sets RTS in order to control the distant site
                    that is supposed deaf to this signal.
        [/EC]     = "r<E>mote <C>lear_to_send": The distant site is supposed to
                    check its CTS signal before its TRANSMITTING, this to
                    control the speed of its transmit flow upon the order of
                    the local site; however, the local site must not interpret
                    the local CTS before its own TRANSMITTING. The local site
                    sets RTS in order to up-date the CTS signal of the distant
                    site.


                                                                       10



        [/BC]     = Use the RTS/CTS hardware hand-shaking in bilateral.
                    (i.e. "<B>ilateral <C>lear_to_send")
        [/LD]     = "<L>ocal <D>ata_terminal_ready": The local site must
                    recognize the DTR/DSR hand-shaking: it checks DSR=TRUE
                    before any send, but it sets DTR in order to control the
                    distant site that is supposed deaf to this signal.
        [/ED]     = "r<E>mote <D>ata_terminal_ready": The distant site is
                    supposed to check its DSR signal before TRANSMITTING,
                    this to control the speed of its transmit flow upon the
                    order of local site; however, the local site must not
                    interpret the local DSR before its own TRANSMITTING. The
                    local site sets DTR in order to up-date the DSR signal
                    of the distant site.
        [/BD]     = Use the DTR/DSR hardware hand-shaking in bilateral.
                    (i.e. "<B>ilateral <D>ata_set_ready").
        [/RI]     = The local site must check that RI=TRUE before TRANSMITTING.
                    REMARK: Check the remark below !
        [/CD]     = The local site must check that DCD=TRUE before TRANSMITTING.
                    REMARK: In fact, it goes of it precisely in the same way
                    for the options [/LC] (with the CTS signal) and [/LD]
                    (with DSR) that are explained,higher, in the context of the
                    normalized protocols RTS/CTS and DTR/DSR. (There is no
                    obligation in the act that local CTS is hardback to remote
                    RTS; or that local DSR has connected to distant DTR !...).
        [/OT]     = The local site set OUT1=FALSE as soon as it is not able
                    to receive anymore data. Otherwise, it sets this signal
                    to TRUE.
                    Analogous REMARK to the previous for [/EC] (RTS signal)
                    and [/ED] (DTR signal).
        [/LX]     = "<L>ocal <X>on/Xoff": The local site knows the Xon/Xoff
                    hand-shaking. But no Xon or Xoff code will be transmitted
                    toward the distant site, supposed deaf to this protocol.
        [/EX]     = "r<E>mote <X>on/Xoff": The distant site is supposed to
                    recognize Xon/Xoff to manage its transmissions on order
                    of the local site; however, the local site doesn't
                    interpret the Xon and Xoff codes that it receives, but
                    must manage them like any other data.
        [/BX]     = Use the software Xon/Xoff hand-shaking in bilateral.
                    (i.e. "<B>ilateral <X>on/Xoff").
        [/X=[<Xon>][,< Xoff>]] = Use the hexa. values specified for
                    the Xon codes (before the comma) and Xoff (after the
                    comma). The values kept by default are 11h (for Xon) and
                    13h (for Xoff). Every hexa. value specified must be
                    made of 2 numbers included between the values 0 and F !

      The following option doesn't have any sense except when STARCOMM is used
    as a DEVICE DRIVER:
        [/ND=xxxxxxxx] = Logical <N>ame of the <D>evice. Permits to assign a
                    different name than "COMM:" to the unit created by STARCOMM
                    when it is loaded from the CONFIG.SYS. It is possible to
                    define this name with this option at any moment using
                    STARCOMM.EXE from the DOS prompt, under the simple
                    condition that STARCOMM resides in RAM as a DOS DEVICE
                    DRIVER. Only the characters 'A'..'Z' and '0.'..'9' are
                    admitted in order to constitute the logical name of
                    STARCOMM used as a DEVICE DRIVER ! This name could be
                    constituted of a number of any active characters included
                    between 2 and 8.


                                                                       11



      The following option is special to a specific type of multi-comm cards:

        [/AP<adress>=<val>] = The <val> byte (hexa.) is sent to the <adress>
                    adresse (hexa.). This permit to activate more than 2 serial
                    ports on specifics multi-ports asynchronous I/O cards.
                    This option may be used more than once (always with the
                    same adress or with differents adresses each time...).
                    ATTENTION: There is no check on the neutral and not dange-
                    -rous type of accessing the specified I/O adress...
                    Only use this option IF YOU KNOW WHAT YOU ARE DOING ! ...

      The 2 following options surpass and nullify all the others options;
    on the other hand, they are not executable by STARCOMM when it is used
    as a DEVICE DRIVER:

        [/D]      = <D>esactivate AND UNINSTALL the driver from the RAM memory.
                    If a program executed after STARCOMM rerouted at least one
                    of the STARCOMM used interrupts (anyone, hard OR soft...)
                    this option won't be treated. A message of impossibility
                    will appear, and it will reacts the same if STARCOMM
                    is used as a DEVICE DRIVER, or if one (or several)
                    program(s) forbade STARCOMM to leave the memory.
        [/?]      = Demand a display of the helping and informations page.
                    This page will be displayed only if STARCOMM is executed
                    from the DOS prompt.

      Finally, the [/PM] (No <M>essage) option permits to forbid the writing
    of the initializations control messages that finally took place. This
    option is especially usefull when we want to avoid the proliferation of the
    messages at the boot time (loading of STARCOMM from the CONFIG.SYS or the
    AUTOEXEC.BAT) ! Only the essential messages of success to install or of
    impossibility to install (or to uninstall) could appear despite this "/PM"
    option. To the contrary, the [/PA[=<length>]] option permits to force
    a <PA>use in order to allow the reading of the driver installation
    report. (<length> admitted from 0 to 60 seconds, 0 for an infinite
    expectation of hitting a key. 0 is the default used value...).

      NOTE that, even though STARCOMM is loaded as a DEVICE DRIVER, it
    remains possible to execute STARCOMM.EXE at any time from the DOS prompt
    in order to command somme new initializations or new working modes
    to the driver installed in memory. All the options, "/D" excluded,
    are perfectly usable in this case.

      All these options could be enumerated in an any order.

      It is possible to modify the status of the driver thanks to these
    commands even though it is already installed in RAM memory.

      The spaces introduced in a command-line don't have any particular
    meaning to the "eyes" of the commands sensor inserted in the serial
    driver. They will always be unknown: you can therefore use spaces at your
    own discretion in order to give your line a more explicit meaning
    to YOUR eyes.

      A request for an helping page provokes the interruption of the program
    immediately after the information is displayed: it will be necessary to
    execute again the driver with the needed options (and, this time, without
    the "/?" option) in order to get the appropriate requested installation.


                                                                       12



      If some contradictory requests are enumerated,only the last valid request
    of the concerned option will be restraint. Besides, it is always the last
    valid declared option (in a given type) that will be served and not its
    previous apparitions in the command-line. For example, "/I1=5,2=3 /I2=7"
    will provoke the utilization of IRQ5 for the COM1: AND of IRQ7 for the
    COM2: !... Exception: the command options of the hand-shaking controls
    activity are cumulatives. For example, "/LX/EX" does have the same effect
    than "/BX".

      The values kept by default are, for each option:
         Addresses--> COM1: 03F8 COM2: 02F8 COM3: 03E8 COM4: 02E8
                      COM5: 01A8 COM6: 01E8 COM7: 01F8 COM8: 02A8 on PC, XT,
                AT--> COM1: 03F8 COM2: 02F8 COM3: 3220 COM4: 3228
                      COM5: 4220 COM6: 4228 COM7: 5220 COM8: 5228 on PS/ 2
               IRQ--> COM1: 4 COM2: 3 COM3: 4 COM4: 3
                      COM5: 3 COM6: 3 COM7: 3 COM8: 3
                      on PC, XT, AT
                      except COM3: 3 (instead of 4) on a PS/ 2
         Speed/Format                 --> 9600 bds, N81, fully UN-locked...
         Ports to be unaware of       --> Not any one.
         BIOS Emulator                --> Inactive.
         Utilization of the FIFO      --> YES with 14 bytes.
         Substitution process         --> Inactive (working in Smode0).
         Receipt buffer               --> 1 kilo-byte.
         Transmit buffer              --> 1/2 kilo-byte.
         Time-out in receipt          --> 10 seconds.
         Time-out in transmit         --> 10 seconds.
         Activity of the hand-shaking --> All inactive (hard and software).
         Codes Xon and Xoff           --> Xon=11h and Xoff=13h.
         Name of DEVICE               --> COMM:
         Physical serial port accessed by COMM:  --> COM1:
      When an option provided to STARCOMM.EXE is not correct, it uses the
    default value of the parameter associated to the deficient control, but
    it doesn't write any message of specific mistake. Just by checking all the
    inits messages (except utilization of "/PM" !) you can assure yourself
    of your command(s) success...

      STARCOMM.EXE systematically disactivates the "user interrupt" functions
    on all the serial ports, as well as the "error management function" of the
    interrupt 14h when it is executed. The BIOS emulator is always DISACTIVATED
    too by default.


                                                                       13



  IV- USING SPECIFIC(S) DEVICE(S) ON SERIAL PORT(S)
  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      1- Using a mouse in 'competition' with STARCOMM:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      þ Install the serial driver with the parameters you really need,
    enumerated in addition to the option "/G<i>" (where 'i' gives the number
    of the port to reserve for the mouse).
      þ Install MOUSE.COM on the serial port your mouse is attached to.
      þ In case of requiring, you could use STARCOMM.EXE all over again in
    order to modify the installation parameters of this driver, but ALWAYS
    INCLUDING the "/G<i>" option in your command-line !
      Indications: This is due to the dynamic management of the environment
        practiced by the driver. In the present case of modifications of the
        inits, whereas an other driver set intervenes (the one of the mouse),
        it makes necessary to protect the inits associated to this other
        driver. This is made by forbidding to our driver the access to
        the port(s) dedicated to the other(s) driver(s). In order to
        interrupt the utilization of the mouse and recover its port to the
        level of our driver, it is sufficient to execute STARCOMM.EXE all
        over again, SUPPRESSING the "/G<i>" option.
        ATTENTION: The most recents mouse drivers MUST be uninstalled because
        they are able to recover their IRQ and inits. dynamically !...



      2- Accessing to an internal or external modem:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      The STARCOMM driver of SERIAL PORTS MANAGER permits to reach any modem
    plugged in any of the serial ports numbered from COM1: to COM8:.
    It is sufficient, for that, to normally install the driver in memory.
      REM: In order to send some specific commands to the modem connected on
      the serial port of your choice, uses the function 1Ah of STARCOMM.
      (i.e., in Pascal and in C, the 'WriteCmde' procedure).
      ATTENTION: When this function 1Ah uses the DTR signal in order to
      indicate the modem that it is going to receive a control, and not a
      sequence of bytes to send on the line, it is necessary that the modem
      receives (before BEING connected) an order indicating not to interpret
      the DTR change to 0 as a connect aborting request ! (For the
      Compatible Hayes modem, the command is AT&D1...). The alternative
      consists in using the function 1Ah with BH=0 (=> DTR no used), and in
      including the prefix of associated command to the modem ("+" by default
      for the Compatible Hayes modems). Report to MODEM.DOC and its examples
      (in PASCAL and C) to this topic.



      3- All type of devices knowing a protocol:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      It goes of it precisely like for the modems.
      Question: Particular case as examples ?
      Answer: The MINITEL with its TeleTex commands,
              the serial printers, ...
              and a lot of other materials (...from laboratories generally !)


                                                                       14



  V- SETPORT.COM UTILITY
  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
      The STARCOMM installation module doesn't permit a selective
  initialization between the various serial ports acknowledged by the driver.
  The reach is global to all the ports supported by the driver... SETPORT
  gives this selective interfacing. Further more, the only functional
  parameters of STARCOMM that SETPORT modifies are those explicitly (and
  correctly) specified in the command-line ! There is not any systematic ini-
  -tialization of all the working variables to their default values like the
  STARCOMM installation/modification module does. Finally, in case of
  contradictory options, it is always the last stated option that carries it
  away, except for the hand-shaking command options that are cumulatives
  (/LX/EX will have the same effect than /BX for example...).
      SETPORT.COM uses the interfacing functions of the driver (interrupt 14h)
  in order to communicate with it and thus to modify its working modes and
  status. This permits, therefore, to demonstrate the good working of these
  service functions of the STARCOMM.EXE serial port driver.



      1- Syntax of SETPORT.COM:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A NOT EMPTY command-line is COMPULSORY. The "/?" command option
    recalls an helping message on the available options, and interrupts the
    utility (all other controls associated to "/?" are ignored):
 d>[<drive>:][<\path\>]SETPORT [<parameter(COM1)>][<parameter(COMi)>...][/I]
    where [COMi:][,<speed>][,<parity>][,<bits>][,<stop>] [/<options>]
    constitutes every group [<parameter(COMi)>] (any space forbidden !).

      If STARCOMM is NOT found available in memory, SETPORT.COM protests by an
    error message and immediately stops.

      If STARCOMM is available and that SETPORT received no command to
    execute, it presents some lines explaining the utility of this program.
    IF all the commands given to SETPORT are unvalid, there will be a
    specific error message; but if at least one command is correct, the
    erroneous command(s) will be merely unknown(s) while the correct(s)
    command(s) will be served...



      2- Command options of SETPORT.COM:
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      The 8 following options have a global reach because they don't concern
    a port in particular:

      [/Inform] (or [/I]) = display an array on the status of the serial
                 ports acknowledged as "existing" (Cf. the introduction of
                 this document). Only the first letter of word "Inform"
                 is sufficient for that option to be acknowledged (ex:
                 "/Infos" will be also admitted !). The written array allows
                 you to check the good acceptance of your commands.
      [/8]     = Display the infos. on the 8 ports.
      [/PC| XT| AT] = Force the recognition of the material architecture.
                 (Cf. same options made more explicit for STARCOMM.EXE).
      [/EB]    = Activate the <E>mulator of the original comm. <B>ios.
                 (report to the explanation of the option "/EB" in page 7
                 of present document...).


                                                                       15

      [/PEB]   = <P>lease, set <E>mulation of original Comm. <B>ios OFF...
                 (that is: desactivation of the BIOS emulator !)
      [/COMM=x]= Makes to point the logical port created by STARCOMM (when
                 it is loaded as a DEVICE DRIVER) on the specified serial port
                 (/COMM=2 will make to use the COM2: by the DEVICE...).

      The following options don't make any sense but when they constitute a
    group clearly identified (a group concerns 1 port identified by "COMi":,
    and it doesn't contain ANY space !):

      [COMi:]  = Announces the definition of the format initializations for the
                 serial port number i (i from 1 to 8 in order to designate
                 from COM1: to COM8:).
      [speed]  = {110,150,300,600,1200,2400,4800,9600,19200,28800,38400,57600,
                 or 115200} bits by second (9600 by default).
      [,parity]= {N, P, I, T, or R} for 'N' no, 'P' even, 'I' odd, 'T' work,
                 or 'R' rest (N by default).
      [,bits]  = {5,6,7 or 8} for a coding on 5, 6, 7 or 8 bits (8 by default).
      [,stop]  = {1 or 2} for 1 or 2 stop-bit(s) (1 by default).
      [/L-]    = Where "-" worth from 0 to 3: L0 makes a complet unlocking,
                 L1 sets the speed locking, L2 the format locking, and L3
                 locks the speed AND the format for the specified port...
                 Notice that SETPORT.COM (like STARCOMM.EXE) doesn't
                 take care of these locking: it may change any speed
                 and format for any port at any time !
      [/A=xxxx]= Definite a new address (HEXA) to associate to the port.
      [/I=x]   = Definite a new IRQ to use (2 to 5, 7, 10 to 12, or 15).
      [/AI]    = <A>utomatic <I>RQ research of IRQ associated to the ports.
      [/G]     = Forbade the access to the port: it then becomes INEXISTANT.
                 This option could not be executed if the IRQ associated
                 to the concerned port was captured by a program executed
                 after STARCOMM.
      [/PG]    = Permits (if possible) the access to the port that becomes
                 existing again (same remark than for "/G" on the IRQ).
      [/PF]    = <P>ort <F>IFO: if the port's UART is a 16550, it will
                 be used in its 8250 emulation mode. Useful for some (old)
                 PS/2 that uses some buggies 16550-A !
      [/F=xx]  = Size of FIFO: 0, or 2 to 15 bytes. "/F=0" is equivalent
                 to "/PF" (see previous...).
      ATTENTION: The options /A /L /AL /PF and /F closes the port by
                 authority !
      [/EL]    = Activate the s<L>ow transmits.
      [/ER]    = Activate the <R>apid (fast) s<E>nds (transmits).
      [/PS]    = No <S>ubstitutions of the bytes received with an error
                 signalled on their transmission.
      [/S]     = Activate the <S>ubstitution of the bytes received with
                 an error by the code 0FEh (the 'þ' character...).
      [/S=Null]= <S>ubstitutions by the empties: all erroneous byte in
                 receipt is not placed in the receipt buffer.
      [/S=xx]  = <S>ubstitutions by the HEXA code xx.
      [/K=xx]  = For each Brea<K> received, make the xx HEXA code appearing
                 in the receipt buffer. /K=Null stops this function. /K
                 (alone) will activate it with the standard value of 03h...
      [/R=xxx] = Time-out <R>ecept after xxx half a second.
      [/E=xxx] = Time-out s<E>nd after xxx half a second.
      [/NC]    = Stop the RTS/<C>TS protocol.
      [/LC]    = Activate the <L>ocal hand-shaking by RTS/<C>TS.
      [/EC]    = Activate the r<E>mote hand-shaking by RTS/<C>TS.
      [/BC]    = Activate RTS/<C>TS in <B>ilateral working.
      [/ND]    = Stop the DTR/<D>SR protocol.
      [/LD]    = Activate the <L>ocal hand-shaking by DTR/<D>SR.
      [/ED]    = Activate the r<E>mote hand-shaking by DTR/<D>SR.
      [/BD]    = Activate DTR/<D>SR in <B>ilateral working.


                                                                       16



      [/NRI] [/RI] = Stop/activation of hand-shaking based on RI.
      [/NCD] [/CD] = Stop/activation of hand-shaking based on DCD.
      [/NOT] [/OT] = Stop/activation of hand-shaking based on OUT1.
      [/NX]    = Stop <X>on/Xoff protocol.
      [/LX]    = Activate the <L>ocal hand-shaking by <X>on/Xoff.
      [/EX]    = Activate the r<E>mote hand-shaking by <X>one/Xoff.
      [/BC]    = Activate <X>on/Xoff in <B>ilat‚ral working.
      [/X=[xx],[yy]]= Definite the HEXA codes to use for Xon ([xx])
                 and Xoff ([yy]).
      [/O]     = <O>pen the port.
      [/F]     = Close the port.

    EXAMPLE: C:> SETPORT COM1:110,p,7,2/s=Null/El/o  COM3:/BX/R=2/AI  /Info


                                                                       17





                    ANNEX A:  Principle of the null-modem cable





      The null-modem cable to use in order to exploit the SERIAL PORTS MANAGER
    driver as well as the associates demos., must be made following
    the minimum installation below:
            (3) Rx (receipt)ÄÄÄÄÄÄÄÄ®®ÄÄÄÄÄÄÄÄ(transmit) Tx (2)
            (2) Tx (transmit)ÄÄÄÄÄÄÄÄÄ¯¯ÄÄÄÄÄÄÄ(receipt) Rx (3)
            (7) Gnd (ground)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(ground) Gnd (7)



      The following installation allows to neutralize the RTS/CTS and DTR/DSR
    signals (allows to verify the neutrality of the hard hand-shaking protocols
    implemented in STARCOMM.EXE):
            (3) Rx (receipt)ÄÄÄÄÄÄÄÄ®®ÄÄÄÄÄÄÄÄ(transmit) Tx (2)
            (2) Tx (transmit)ÄÄÄÄÄÄÄÄÄ¯¯ÄÄÄÄÄÄÄ(receipt) Rx (3)
            (7) Gnd (ground)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(ground) Gnd (7)
            (4) RTS¯Ä¿                               ÚÄ®RTS (4)
            (5) CTS®ÄÙ                               ÀÄ¯CTS (5)
           (20) DTR¯Ä¿                               ÚÄ®DTR (20)
            (6) DSR®ÄÙ                               ÀÄ¯DSR (6)



      In all rigor, the complete scheme for the null-modem cable is:
            (1) Chassis ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Chassis (1)
            (3) Rx (receipt)ÄÄÄÄÄÄÄÄÄ®®ÄÄÄÄÄÄÄ(transmit) Tx (2)
            (2) Tx (transmit)ÄÄÄÄÄÄÄÄ¯¯ÄÄÄÄÄÄÄÄ(receipt) Rx (3)
            (7) Gnd (ground)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(ground) Gnd (7)
            (4) RTS ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¯¯ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ CTS (5)
            (5) CTS ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ®®ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ RTS (4)
           (20) DTR ÄÄÄÄÄÄ¯¯ÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄ®®ÄÄÄÄÄÄ DTR (20)
            (6) DSR Ä®Ä¿             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄ¯Ä DSR (6)
            (8) DCD Ä®ÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ          ÀÄ¯Ä DCD (8)
           (22) RI ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ RI (22)


                                                                       18





      There is, between the number of the DB25 binds (concerned by the above
    diagrams) and the number of the DB9 bind, the following corresponding:

           Taken DB9                   Taken DB25    Signal
               3----------------------------2   <-->   Tx
               2----------------------------3   <-->   Rx
               5----------------------------7   <-->   Gnd
               7----------------------------4   <-->   RTS
               8----------------------------5   <-->   CTS
               6----------------------------6   <-->   DSR
               4----------------------------20  <-->   DTR
               1----------------------------8   <-->   DCD
               9----------------------------22  <-->   RI



   !!!!!!!!!!!!!!!!!!  T A K E    C A R E   ---> Users... !!!!!!!!!!!!!!!!!
   !!!    All other type of NULL MODEM CABLE is susceptible of          !!!
   !!! provoking some stops of communication between the programs       !!!
   !!! using the serial driver STARCOMM.EXE v2.0 and above. The risk    !!!
   !!! entirely rest on the nature of the used links (by the cable)     !!!
   !!! between the communication control signals...                     !!!
   !!! If your cable is not suitable, do not use the options to activate!!!
   !!! any of the hand-shaking protocols RTS/CTS, DTR/DSR, RI, etc...   !!!
   !!!!!!!!!!!!!!!!!!!!!!!!!!!!!!! Developers... !!!!!!!!!!!!!!!!!!!!!!!!!!
   !!!    You could define some particular hard hand-shaking            !!!
   !!! (following the developed instructions in STAR_REF.DOC ANNEX...). !!!
   !!! Using its personalized management of modem signals, your program !!!
   !!! won't be able to work without its cable to the particular        !!!
   !!! pattern: you will have earned a good hardware KEY protection for !!!
   !!! your program...                                                  !!!
   !!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!


                                                                       19





            ANNEX B:  Types of UART chips on PC and compatibles



       This appendix present a fast summary on the types of UART, products by
     INTEL Cø (tm) and compatible with the 8250, that was successively
     implemented on the range of IBM computers and compatibles.

       8250 ......... First UART used on the first IBM PC. It is a slow
                      controller: the accesses to the registers are faster
                      than the treatments done by the 8250 ! It disposes of
                      7 registers and is "sold" in order to accept bauds until
                      56 Kilo-bauds. The receipt and transmit buffer are
                      both made of only one byte.
       8250A ........ It is a correction of 8250, with 1 register in addition:
                      the scratchPad, that allows to mark the presence of
                      the UART controller.
       16450 ........ It is an improved version of 8250A: its internal
                      treatments are fast enough in order to avoid some losses
                      of time at the time of software accesses to the
                      controller regiters. It doesn't permit however, in
                      theory, to support more than a 56 kilo-bauds speed of
                      transmission.
       16C451 ....... It is the CMOS version of 16450 (i.e. 16450 with low
                      electric energy needs).
       16550 ........ First version of a new improved 16450: it should permit
                      the activation of an internal buffer of 16 bytes,
                      and the support of 256 kilo-bauds. A mistake in
                      realization made it inoperative. Only some first
                      PS/2 received this controller (quickly retired from
                      INTEL Cø !). It must NOT be used as a 16450 (i.e.
                      forbid the activation of its FIFO mode using the /PF
                      option of STARCOMM.EXE !).
       16550A/AF/AFN. It is the first functional version of 16550 ! Its 16
                      bytes buffers do works and it support up to 256 Kilo-Bds.
       16C551 ....... CMOS version of 16550AF.
       16C552 ....... Implement 2 16C551 in the same electronic box.
       82510 ........ It is a 16450 supplied with buffers of 4 bytes. It is
                      used in some notepad.
       Then.......... It decorated how certain(s) competitor(s) of the INTEL
                      business is attacking the production of 16550AFN type
                      controllers, based on the utilization of 32 bytes in
                      its internals buffers (this since mis-1990...).
                      To follow !...

       To summarize, retain 3 generations in the evolution of this UART
     controller essentially (Universal Asynchronous Receiver & Transmiter)
       8250A ........ Simple but slow UART,
       16450 ........ Simple and fast UART,
       16550AF ...... Fast UART, with 16 bytes buffers and reliable !


                                                                       20





                       ANNEX C:  Why a "BIOS emulation" ?





       Why offering an option to emulate the BIOS interrupt 14h whereas
     STARCOMM.EXE seem already be (by nature) such an emulator ? Because the
     functions 1 (send) and 2 (receive) of the INT 14h filtered by STARCOMM
     could benefit from contributions of this driver (16550 UART FIFO buffers
     excepted) only with the OPENED ports of the driver. Indeed, STARCOMM
     redirects the calls to these functions for the closed serial ports on
     the original BIOS interrupt (it was a logical choice at the time of the
     initial program development !...).

       In order to benefit from the possible redistribution of some serial
     ports addresses, from the access to the ports 1 up to 8, from the time-out
     definitions, and from hardware (input/output) hand-shakings, even on
     STARCOMM CLOSED ports, it is therefore necessary to activate a special
     part of the driver code: its BIOS emulator of the original BIOS
     communication functions.
       Of course, the I/O serial ports buffers won't be used when accessing
     a closed port THROUGH the BIOS emulator (it is necessary and sufficient
     to OPEN the ports in order to fully benefit from STARCOMM contributions !)
     But this emulation permits to dispose of an improved BIOS (from the today
     available UART point of view) as soon as STARCOMM.EXE is installed on
     your machine with its BIOS emulator activated...
       This improved BIOS also guaranties a security on the used addresses in
     order to reach to the UART (it is not anymore the BIOS addresses specified
     by [40:00] to [40:06] that is used, but the driver addresses, well
     "hidden" in RAM !). It finally permits to enhance all PC compatible BIOS
     with the function 05h that doesn't normally exist, except on the PS/2...


                                                                       21





             ANNEX D:  Files making SERIAL PORTS MANAGER v2.20





        INFORME  DOC...General informations on the product origin.
        SPECIFS  DOC...General technical facts on the pack.
        REGISTER DOC...To register SERIAL PORTS MANAGER, send me your
                       appreciations, or report some noted bugs.
        UPDATES  DOC...What's new in this last release of S.P.M. ?...
        STARGUID DOC...The user guide for SERIAL PORTS MANAGER v2.20
        STAR_REF DOC...The reference manual for programming by using
                       STARCOM8.EXE, STARCOMM.EXE or SCLIB.OBJ.

        SETPILOT  EXE..Small utility to install and setup STARCOMM.EXE

        STARCOMM EXE...Serial driver:it is the kernel of SERIAL PORTS MANAGER !
        STARCOM8 EXE...Kernel of SERIAL PORTS MANAGER adapted to the management
                       of 8 serial ports (STARCOMM can only drive up to
                       4 serial ports...).
        SETPORT  COM...An utility developed (using C) in order to offer you
                       a way to have a 'port by port' control on the installed
                       driver in memory (whereas it works in its BIOS or
                       DEVICE DRIVER mode).
        STARINTF PAS...Interface in order to use the driver services from
                       the (C)Turbo Pascal.
        STARINTF C.....Interface in order to use the driver services from
                       the (C)Turbo C.
        SCLIB    OBJ..."Library" release of STARCOM8.EXE (8 ports).
        DEMO_LIB ASM...A simple demo. of how to use SCLIB.OBJ.

        TESTSTAR PAS...A demo. DEVELOPED in Turbo PASCAL to use STARCOMM
                       in a multi-communication process.
                       Require the procedures of STARINTF.PAS
        TESTSTAR EXE...Executable file of this demonstration !
        TERMINAL C.....A simple TTY terminal based on the use of STARCOMM
                       loaded as a DEVICE DRIVER: we reache the port by
                       the means of the logical file (called "COMM:").
                       Require the procedures of STARINTF.C
        TERMINAL COM...Executable file of this demonstration !

        REMOTE   EXE...A small application allowing you to exploit a remote
                       IBM PC/AT from the local computer. We could name it
                       a "DOS terminal emulator"...

        MODEM    DOC...Document containing informations on the procedures
                       made to access modems, procedures contained in
                       MODEM.PAS and MODEM.C.
        MODEM    PAS...PASCAL procedures to access HAYES modems.
        MODEM    C.....C procedures to access HAYES modems.
        TESTMODP PAS...Source of the demo. to use MODEM.PAS.
        TESTMODC C.....Source of the demo. to use MODEM.C.

        CONVERT  DOC...Document for the procedures made to convert data.
        CONVERTA ASM...Simple procedures to make ASCII-transcoding: they
        CONVERTP PAS...permit to transfer any binary file even when using
        CONVERTC C.....the Xon/Xoff software hand-shaking...