STARTUP.SYS for OS/2

         Soundblaster StartUp Sound  -  Copyright (c) 1995 Robert Muchsel
         Internet: muchsel@acm.org

         Release 1.00


         True StartUp Sound for OS/2
         ---------------------------


         Freeware (see end of this file).


         OS/2 has a built-in startup sound. However, the sound requires
         the MMPM/2 overhead and is played only when the system is up and
         running.

         That's not startup!

         This OS/2 base device driver plays a startup sound on your
         Soundblaster card (or compatible) as soon as the OS/2 logo is
         displayed! Plus, it doesn't require the massive MMPM/2 overhead
         and randomly selects one out of six cool sounds. It does not
         interfere with MMPM/2.

         This software works on my Soundblaster Pro and Vibra 16 cards and
         has been tested on many PCs. However, I cannot guarantee anything
         and you will be using it at your own risk.



         Installation
         ============

         Put STARTUP.SYS into the \OS2\BOOT directory of your boot drive
         (or \OS2 if you are using OS/2 2.x).

         Add the line

            BASEDEV=STARTUP.SYS /SWITCHES

         to the TOP of your CONFIG.SYS (Mozart card users: Put it one line
         below your mozart.sys card enabler). The /SWITCHES are discussed
         below.


         Switches
         --------

            /P: Port address (default: 220)
            /D: DMA channel (default: 1)
            /I: Interrupt (default: 5)
            /V: Volume (default: 13)

         The volume switch is only supported if your Soundblaster card has a
         mixer.

         Examples:

           BASEDEV=STARTUP.SYS /V:15
           BASEDEV=STARTUP.SYS /P:240 /I:10


         Reboot. OS/2 will take care of the rest. Have fun!




         Licence
         =======

         Developing this driver has taken a considerable amount of time,
         especially getting OS/2 to do DMA in a base device driver.
         Despite of that, this software is free.

         However, if you (rightly) feel that you should donate some money
         or OS/2 development tools, please don't hesitate.

         My postal address is:                          Internet:

           Robert Muchsel                                 muchsel@acm.org
           Hegaublick 2
           78465 Konstanz
           Germany

         Please do understand that I cannot answer any letters if you don't
         cover the return postage. E-mail is preferred, definitively.

         You might want to donate something to Amnesty International
         instead.


         Important
         ---------

         The author disclaims all warranties as to this software, whether
         express or implied, including without limitation any implied
         warranties of merchantability, fitness for a particular purpose,
         functionality, data integrity or protection, in so far as permitted by
         applicable legislation.

         All trademarks are property of their respective owners and appear for
         identification purposes only.

         You are encouraged to copy and pass on this program. However,
         - the program must be distributed in its original form
           (complete, unmodified)
         - the distribution must not exceed the equivalent of DM 15.-
           (US$ 8.50).

         28 Dec 1995