Personal Communications Library

                           For Windows


                             (PCL4W)



                          USERS MANUAL





                           Version 1.3

                           July 8, 1996




                 This software is provided as-is.
          There are no warranties, expressed or implied.




                       Copyright (C) 1996
                       All rights reserved



                   MarshallSoft Computing, Inc.
                       Post Office Box 4543
                       Huntsville AL 35815

                       Voice : 205-881-4630
                         FAX : 205|880|0925
                         BBS : 205-880-9748
                       email : info@marshallsoft.com
                         web : www.marshallsoft.com

                           _______
                      ____|__     |                (R)
                   --+       |    +-------------------
                     |   ____|__  |  Association of
                     |  |       |_|  Shareware
                     |__|   o   |    Professionals
                   --+--+   |   +---------------------
                        |___|___|    MEMBER














 PCL4W Users Manual                                                Page 1
                       C O N T E N T S





  Chapter                                                   Page

  1.0 Introduction................................................3
      1.1 User Support............................................4
      1.2 ASP Ombudsman...........................................4
      1.3 A Typical Application...................................5
      1.4 Determining UART Address & IRQ Settings.................6
      1.5 Disabling Windows Ports.................................6
      1.6 Installation............................................7
  2.0 Library Organization........................................8
      2.1 Configuration...........................................8
      2.2 Initialization & Termination............................8
      2.3 Modem Control & Status..................................9
      2.4 Serial I/O..............................................9
      2.5 Error Detection........................................10
      2.6 General Support........................................10
  3.0 Library Overview...........................................11
      3.1 Dynamic Link Libraries.................................11
      3.2 DOS Protected Mode Interface...........................11
      3.3 Memory Models..........................................11
      3.4 Using the Library......................................11
      3.5 Using a MAKEFILE.......................................12
      3.6 Using an IDE...........................................12
      3.7 Making the Library.....................................12
  4.0 Talking to Your Modem......................................13
      4.1 Modem Standards........................................13
      4.2 Flow Control...........................................14
      4.3 Modem I/O Functions....................................15
      4.4 Modem Initialization...................................17
  5.0 Problems...................................................18
  6.0 Serial Communications......................................19
      6.1 Communications Basics..................................19
      6.2 Standard Port Addresses................................20
      6.3 Running 3 or 4 Ports Concurrently......................21
      6.4 Using Multiport Boards.................................22
          6.4.1 Using the Digiboard..............................22
          6.4.2 Using the BOCA board.............................22
      6.5 Transmitter Interrupts.................................23
      6.6 RS232 Signals..........................................24
      6.7 National INS8250, INS16450, and INS16550 UARTs.........25
      6.8 Register Summary.......................................26
  7.0 Example Programs...........................................28
      7.1 SIMPLE.................................................28
      7.2 LOGIN..................................................28
      7.3 SELFTEST...............................................28
      7.4 TERM...................................................28
  8.0 Legal Issues...............................................29
      8.1 Registration...........................................29
      8.2 License................................................30
      8.3 Warranty...............................................30
  9.0 Summary....................................................31
      9.1 Revision History.......................................31
      9.2 Function Summary.......................................32
      9.3 Further Reading........................................33
 10.0 Other MarshallSoft Computing products for C/C++............33
      10.1 The Personal Communications Library for C/C++.........33
      10.2 Libraries for Other Languages.........................33




 PCL4W Users Manual                                                Page 2
  1.0 Introduction


  The  Personal  Communications Library for Windows (PCL4W) is an asynchronous
  communications dynamic link library (DLL) for software developers using  the
  Microsoft  Windows  C/C++  compiler,  the  Borland  Windows compiler, or the
  WATCOM Windows compiler. Other Windows compilers may  also  work.   A  80386
  machine or higher is recommended.


  o 30+ communications functions.
  o Supports the high performance INS16550 UART.
  o Supports the PC/4 and PC/8 DigiBoard.
  o Supports the BOCA BB1004, BB1008, and BB2016 boards.
  o Supports hardware (RTS/CTS) flow control.
  o Use any IRQ (IRQ0-IRQ15) with any UART address.
  o Interrupt driven receiver & (optionally) transmitter.
  o Supports 300 baud to 115,200 baud.
  o Supports COM1 through COM20.
  o Adjustable queues from 8 bytes to 32 KB.
  o Control-BREAK error exit.
  o 18 communications error conditions trapped.
  o Allows 4 ports to run concurrently (more with Digi/BOCA board).
  o Complete modem control & status.
  o Written in assembly language for small size & high speed.
  o Terminal program featuring ASCII (with XON/XOFF), XMODEM,
    YMODEM, & YMODEM-G.


  Why should you buy PCL4W? Consider the following:

     COMPLETE  :  PCL4W is complete since it provides absolute control of the
                  serial ports (including the high performance INS16550).

      COMPACT  :  PCL4W is very compact at less than 6 KB.  Your  application
                  doesn't carry a lot of excess code.

         FAST  :  PCL4W is fast.  It will run at 115200 baud on all 80386 and
                  up machines.

      SUPPORT   : If  you  get  stuck,   you will talk to the programmer that
                  wrote the code, not a person hired to answer the phone.

          BBS  :  A user support BBS is available (2400 to 14400 baud, N81) in
                  order to provide immediate support as necessary.

   NEWSLETTER  :  Our newsletter "COMM TALK" is published quarterly (available
                  online)   which   discusses   communications   problems  and
                  solutions.

        PRICE  :  You get PCL4W for a very reasonable price !

     UPGRADES  :  Once  you  buy  PCL4W,  you can always update  to  the most
                  recent version for a very reasonable cost.

   COMPATIBLE  :  PCL4W  is  call  for call compatible with the MSDOS based
                  version PCL4C except for two functions in which delay  times
                  are no longer necessary.


  Our goal is to provide a robust serial communications library that that  you
  and your customers can depend upon.





 PCL4W Users Manual                                                Page 3
  1.1 User Support


  We want you to be successful in developing your applications using PCL4W! We
  depend on our customers to let us know what they need  in  a  communications
  library.   This  means we are committed to providing the best communications
  library that we can. If you have any suggestions or comments, please let  us
  know.

  If you are having a problem using PCL4W, call  us  at  205-881-4630  between
  1:30PM  and  9:30PM  CST  Monday  through Friday. You can also call at other
  times and leave a message, and call back  later  for  a  reply.   Registered
  users (ONLY) can also FAX us at 205-880-0925 at any time (24 hours).

  However,  we  can  only  answer  questions  with  respect to using the PCL4W
  library.  We cannot help you program your application.

  You  may  also  call  our User Support BBS (2400 to 14400 baud, no parity, 8
  data bits, 1 stop bit) at 205-880-9748 and leave a message  (address  it  to
  the SYSOP).  We will usually have a reply ready for you within 24 hours.

  The BBS  is  available  24  hours  per  day  except  at  2  PM  Sundays  for
  maintenanace. All files are in standard ZIP format. The BBS will contain the
  latest  shareware  version  of  all MarshallSoft products as well as related
  files such as:

       BUGS.ZIP:  Bug report.
       NEWS.ZIP:  Latest news regarding our products.

  If you are on the Internet, you can email us at info@marshallsoft.com.   You
  can  also  get  the  latest  versions of our products from our anonymous ftp
  site:

        FTP:   ftp.marshallsoft.com
       PATH:   marshallsoft

  The MarshallSoft  Computing,  Inc.   newsletter  "Comm  Talk"  is  published
  quarterly.  It discusses various communications problems and solutions using
  PCL4W  as  well  as related information.

  The   latest   copy   of our newsletter can be found on User Support BBS (in
  file area "Newsletters"), our anonymous ftp site  (directory  /marshallsoft)
  as well as our web site.

      Web site:  www.marshallsoft.com


  1.2 ASP Ombudsman


  MarshallSoft  Computing,  Inc.   is a member of the Association of Shareware
  Professionals (ASP).  ASP wants to make sure that  the  shareware  principle
  works  for  you.   If  you are unable to resolve a shareware-related problem
  with an ASP member by contacting the member directly, ASP  may  be  able  to
  help.  The  ASP  Ombudsman can help you resolve a dispute or problem with an
  ASP member, but does not provide technical support  for  members'  products.
  Please  write  to  the  ASP  Ombudsman  at 545 Grover Road, Muskegon, MI USA
  49442-9427, Fax 616-788-2765, or send a CompuServe  message  via  CompuServe
  Mail to ASP Ombudsman 70007,3536.








 PCL4W Users Manual                                                Page 4
  1.3 A Typical Application


  In general, there are two classes of applications that use a  communications
  library  like  PCL4W: those that use a modem to connect to the outside world
  and those that connect directly to a peripheral device. In  either  case,  a
  typical   application  program  using  PCL4W  might  consist  of  3  phases:
  initialization, execution, and  termination.   The  following  code  segment
  assumes a knowledge of the windows API.

  In  the  following  code  segment,  SioRxBuf is called to set up a 1024 byte
  receive buffer; SioParms is called to set up the parity, stop bit count, and
  word length; SioReset is called to set the baud rate to 9600 and  reset  the
  UART (Universal Asynchronous Receiver / Transmitter).


       case WM_CREATE:
          /* initialization */
          SioRxBuf(Port,RxBuffer,Size1024);
          SioParms(Port,NoParity,OneStopBit,WordLength8);
          SioReset(Port,Baud9600);


  If you are using the version of  the  library  with  transmitter  interrupts
  enabled  (PCL4W2.LIB),  then  SioTxBuf()  must  be  called  to  set  up  the
  transmitter buffer. The transmit buffer must be distinct  from  the  receive
  buffer.


       case WM_CREATE:
          /* initialization */
          SioRxBuf(Port,TxBuffer,Size1024);
          SioTxBuf(Port,RxBuffer,Size1024);
          SioParms(Port,NoParity,OneStopBit,WordLength8);
          SioReset(Port,Baud9600);


  Characters can be  transmitted  and  received  once  the  required  port  is
  initialized.   Before leaving your application, SioDone is called to restore
  the prior state of the serial communications  system.   Forgetting  to  call
  SioDone  before  exiting your application will leave the interrupt system in
  an unuseable state and the machine will have to be re-booted.


       case WM_DESTROY:
          /* termination */
          SioDone(Port);


  If you are using a modem, you also need to be concerned  about  initializing
  your  modem  correctly  and  handling  any  required flow control.  Refer to
  Chapter 4.0, "Talking to Your Modem" for detailed information.















 PCL4W Users Manual                                                Page 5
  1.4 Determining UART Address & IRQ Settings


  Both Windows 3.X and Windows 95 maintain a list of serial port settings.  On
  Windows  3.X  systems, choose the "Ports" icon in the "Control Panel" in the
  "Main Group".  Select "Settings", and then "Advanced" to view the  COM  port
  UART address and IRQ settings.

  In Windows 95, choose "My Computer" icon ("or whatever your computer icon is
  named), select the "Control Panel" folder and then the "System" icon.  Click
  on  the "Device Manager" tab.  Click "Computer" and then click "Properties".
  Click the "View Resources" tab.   To  view  reserved  resources,  click  the
  resource  type at the top of the dialog box (i.e., "Interrupt request (IRQ)"
  or "Input/output (I/O)" ).


  1.5 Disabling Windows Ports


  The Windows operating system virtualizes all serial ports that it  controls.
  This  means  that  Windows  intercepts  reads  and writes to hardware ports,
  resulting in significant slowdown. When Windows virtualizes a port, the UART
  FIFO control register (FCR) can not be modified.

  Since  PCL4W  also  controls the hardware directly, it is best (although not
  absolutely necessary) to disable Windows control of the serial ports and the
  IRQs that will be used by PCL4W applications.

  The four standard COM ports which Windows typically controls are:

        Port  Address  IRQ
        COM1   &H3F8    4
        COM2   &H2F8    3
        COM3   &H3E8    4
        COM4   &H2E8    3

  Since COM1 and COM3 share an IRQ, if either is to be used by PCL4W then both
  should be disabled from Windows control. Similarly for COM2 and COM4.

  To begin, exit from Windows completely. To disable the  serial  ports,  edit
  the  [386Enh] section of the WINDOWS.INI file in the WINDOWS directory.  For
  example, to disable COM1 and COM3,  add  the  following  to  the  [386  Ehn]
  section:

        COM1Base=0
        COM1Irq=-1
        COM3Base=0
        COM3Irq=-1

  Restart Windows after modifying SYSTEM.INI. This procedure does not apply to
  multiport boards or any other serial ports unknown to Windows.

  16550 UARTS are really necessary when running under Windows, particularly at
  baud  rate  above 19200.  The Microsoft Diagnostics (MSD) program can be run
  which will report the type of UARTs installed on your machine.

  If a 16550 port MUST be shared with Windows, and you want the FIFO  enabled,
  look for statements such as

        COM1FIFO=0

  in  the  [386Ehn] section of SYSTEM.INI and delete it.  However, the Windows
  communications driver may have trouble with the FIFO, which is why there  is
  a statement to disable it. This problem does not occur with PCL4W.



 PCL4W Users Manual                                                Page 6
  1.6 Installation


  (1) Before installation of PCL4W , your Windows C compiler should already be
  installed on your system and tested. Examine the file "FILES.LST" for a list
  of the distribution files.

  (2) Make a backup  copy  of  your  distribution  disk.   Put  your  original
  distribution disk in a safe place.

  (3) Create a work directory on your hard drive. For  example,  to  create  a
  work directory named PCL4W, type from DOS:

                   MKDIR PCL4W

  (4)  Copy  all  the  files from your backup copy of the distribution disk to
  your work directory.  For example, to copy from the A: drive  to  your  work
  directory, we type:

                  CD PCL4W
                  COPY A:*.*

  (5)  Compile SIMPLE.C and link with the PCL4W library (PCL4W.LIB).

  Makefiles  and  project  files  are  provided  for  each  of  the  supported
  compilers.

       Microsoft command line compiler:   NMAKE SIMPLE._M_
       Borland command line compiler:     MAKER -fSIMPLE._B_
       Watcom command line compiler:      WMAKE -f SIMPLE._W_

  NOTES: (1) Use NMAKE, not MAKE with Microsoft C
         (2) Use MAKER, not MAKE with Borland C.

  Alternately, SIMPLE can be compiled in an Integrated Development Environment
  (IDE)  such  as supplied by Microsoft, Borland, and Watcom. Refer to section
  3.5 "Using an IDE" for more information.

  (6) The recommended way to test  SIMPLE  is  to  run  it  on  two  computers
  connected  by  a null modem cable.  Whatever is typed on one computer should
  be displayed on the other. If you don't have  two  computers,  you  can  use
  SIMPLE  to talk to your modem. Sending an "AT" to the modem should result in
  an "OK" being sent back. See section 7.1 "SIMPLE" for more information.

  (7) Compile and link LOGIN. Use LOGIN to call a local BBS. See  section  7.1
  "LOGIN" for more information.

  (8)  Compile  and  link  SELFTEST.   Use SELFTEST to test one of your serial
  ports. See section 7.3 "SELFTEST" for more information.


















 PCL4W Users Manual                                                Page 7
  2.0 Library Organization


  The  PCL4W  library  is organized into six categories of functions. Refer to
  the PCL Reference Manual (PCL4W.REF) for details on individual functions.


  2.1 Configuration


  There  are three functions in the configuration category.  SioPorts sets the
  number of PC and DigiBoard / BOCA ports.  SioUART is used to change the UART
  base address for a communications port  to  a  non-standard  address,  while
  SioIRQ  is  used  to  assign a nonstandard IRQ line to a port.  (See Section
  6.2, Standard Port Addresses for more details on standard UART addresses and
  IRQ lines).

  The  configuration  functions  SioPorts,  SioUART  and SioIRQ must be called
  before calling any other library functions.   Be  very  careful  when  using
  these  functions.   Remember that your serial hardware must support the UART
  and IRQ that you specify.  Always test any new configuration immediately.

       SioPorts : Sets number of PC and DigiBoard / BOCA ports.
       SioUART  : Sets the UART base address.
       SioIRQ   : Assigns an IRQ line to a port.

  THE IRQ GOLDEN RULE: You may open (via  SioReset)  only  one  port  per  IRQ
  (except for the DigiBoard / BOCA board).


  2.2 Initialization & Termination


  There  are  nine  functions  in the initialization and termination category.
  Together, SioGetDiv, SioFIFO, SioRxBuf, SioTxBuf,  and  SioReset  initialize
  your  serial communications system.  Your application must call SioParms and
  SioRxBuf before calling SioReset, and SioReset must  be  called  before  any
  serial I/O processing can be done.

  After initialization, SioParms and SioBaud can be called again to change the
  communications  parameters without resetting the serial port. SioFlow can be
  called to enable hardware flow control.

  Before exiting from your application, SioDone must  be  called.  Failure  to
  call SioDone can crash your system later.

       SioRxBuf   : Sets up receive buffer.
       SioTxBuf   : Sets up transmitter buffer.
       SioFIFO    : Sets the interrupt level for the INS16550.
       SioParms   : Sets parity, stop bits, and word length.
       SioReset   : Initialize a serial port for processing.
       SioDone    : Terminates further serial processing.
       SioBaud    : Sets the baud rate of the selected port.
       SioFlow    : Enables / disables flow control.
       SioGetDiv  : Gets the baud rate divisor.












 PCL4W Users Manual                                                Page 8
  2.3 Modem Control & Status


  There  are  eight  functions  in the modem control and status category which
  provide your application with complete control over the status  and  control
  bits of your modem.

  There  are  two modem control bits, "Data Terminal Ready" (DTR) and "Request
  To Send" (RTS). These bits can be  read,  set,  or  cleared  by  SioDTR  and
  SioRTS.

  There  are  four  modem status bits, "Data Set Ready" (DSR), "Clear To Send"
  (CTS), "Ring Indicator" (RI), and "Data Carrier Detect" (DCD). SioModem  can
  read  any  of  the modem status bits.  SioDSR, SioCTS, SioRI, and SioDCD can
  only read their respective modem status bit.

  Refer to the chapter entitled "RS232 Signals" for a discussion  of  each  of
  the control and status bits.

       SioDTR   : Set, clear, or read the Data Terminal Ready (DTR) bit.
       SioRTS   : Sets, clears, or reads the Request to Send (RTS) line.
       SioModem : Reads the modem status register.
       SioDSR   : Reads the Data Set Ready (DSR) modem status bit.
       SioCTS   : Reads the Clear to Send (CTS) modem status bit.
       SioDCD   : Reads the Data Carrier Detect (DCD) modem status bit.
       SioRI    : Reads the Ring Indicator (RI) modem status bit.
       SioRead  : Reads the contents of the 7 UART registers.


  2.4 Serial I/O


  There  are  eight  library  functions  in the serial I/O category. Together,
  these functions give the programmer complete control over serial I/O. Higher
  level functions such as protocols and  smart  modem  communications  can  be
  completely  implemented  in  terms  of these functions. Refer to the example
  code.

  SioGetc and SioPutc perform all the actual serial I/O.   SioUnGetc  "ungets"
  the  last  serial  byte  read.  SioRxClear  clears  the  receive queue while
  SioTxClear clears the transmit queue. SioLine can be used to test  for  UART
  errors.   SioRxQue  returns  the  number of bytes in the receive queue while
  SioTxQue returns the number of bytes in the transmit queue.

       SioGetc    : Reads the next character from the serial line.
       SioPutc    : Transmit a character over a serial line.
       SioUnGetc  : "Un:gets" (puts back) a specified character.
       SioRxClear : Flush (clears) the receive buffer.
       SioRxQue   : Returns the number of characters in the RX queue.
       SioTxClear : Flush (clears) the transmit buffer.
       SioTxQue   : Returns the number of characters in the TX queue.
       SioLine    : Reads the line status register.















 PCL4W Users Manual                                                Page 9
  2.5 Error Detection


  There  are  three  functions  in  the  error  detection  category.  They are
  concerned with detecting or reporting communications errors.  Use  of  these
  functions can make your application significantly more robust.

  SioBrkSig can read or  modify  the  UART  break  bit.  This  is  useful  for
  signalling   the   remote  system  that  a  fatal  condition  has  occurred.
  SioLoopBack can be used to test the integrity of your UART.

  There is also a file SIOERROR.C which contains the function  SioError  which
  displays  a  error  message  corresponding  to an error code returned from a
  PCL4W function (every PCL4W function returns a code).

       SioBrkSig   : Asserts, cancels, or detects the RS232 BREAK  signal.
       SioError    : Displays  error  in  text.
       SioLoopBack : Performs a UART loopback test.


  2.6 General Support


  There is one function in the general support category. SioInfo  returns  the
  version  number  of  the  library  and  whether  transmitter  interrupts are
  enabled.

       SioInfo      : Returns the library version, memory model, the number of
                      transmitter interrupts, and receiver interrupts.






































 PCL4W Users Manual                                                Page 10
  3.0 Library Overview


  3.1 Dynamic Link Libraries


  PCL4W is provided as a dynamic link library (DLL). A DLL is characterized by
  the fact that it need not be loaded until required by an application program
  and that only one copy of the DLL is necessary regardless of the  number  of
  application  programs  that  use it. Contrast this to the traditional static
  library which is bound to each and every application that uses  it  at  link
  time.

  Since  PCL4W is a DLL, only one copy of the PCL4W code & data is loaded into
  memory regardless of the number of applications programs that use it.

  For example, more than one instance  of  the  test  program  SIMPLE  can  be
  started.   All  copies of SIMPLE can run concurrently as long as each uses a
  different COM port.


  3.2 DOS Protected Mode Interface


  Windows itself uses what is known as  the  "DOS  Protected  Mode  Interface"
  (DPMI)  to  control  changing  states  (protected  vs real), controlling the
  interrupt system, etc.  This is necessary because Windows  itself  typically
  runs  in  a  protected  state  and must change to real state in order to use
  MSDOS services.

  The  PCL4W  library  uses  this same DPMI mechanism. In particular, the file
  USE_DPMI.ASM contains the necessary functions for using DPMI. The  developer
  should not modify USE_DPMI.ASM in any way.


  3.3 Memory Models


  Most windows programs are small or medium memory model programs since  these
  memory models are limited to one data segment.  However, all PCL4W functions
  are FAR functions, so they can be used with any memory model. Thus, there is
  just one PCL4W.DLL and PCL4W.LIB regardless of the memory model used.


  3.4 Using the Library


  The  PCL4W has been tested on a Gateway 2000 25 MHZ 80386-DX, a Gateway 2000
  66MHZ 80486-DX2 (all running Windows  3.1),  and  a  Mid-West  Micro  150MHZ
  Pentium running Windows 95.

  PCL4W  has  been  testing  with  the  Microsoft Windows SDK compiler, Visual
  C/C++, Borland C/C++, and Watcom C/C++.

  Please examine the PCL4W.H file. Note that COM1 is defined as port zero, not
  port  one.   The  user must assume the responsibilty for passing the correct
  information when calling PCL4W functions.

  If there are any conflicts between PCL4W  definitions  and  those  in  other
  libraries,  the PCL4W definitions can be changed in the PCL4W.H file and any
  file that uses the definition. There is no change necessary for the  library
  code itself.

  If  you  write  an  application  using  the PCL4W library, don't run another
  application that uses the same communications port.


 PCL4W Users Manual                                                Page 11
  3.5 Using a MAKEFILE


  Makefiles  originated  on UNIX systems. They are the standard way that C/C++
  programs are constructed in command line environments. Windows programs  can
  be  constructed  with  makefiles  running  DOS  using  command  line Windows
  compilers, such as provide by Borland and Microsoft.

  Makefiles are provided for Microsoft and Borland command line compilers.


  3.6 Using an IDE


  All windows comilers have an Integrated Development  Environment  (IDE)  for
  building  application programs in the Windows environment. Since there is no
  standard format for IDE project files, file names must be entered  into  the
  IDE  from  the  keyboard.  Each example program has a project text file (eg:
  SIMPLE.PRJ) which contains the list of filenames that must be  entered  into
  the IDE.

  The  example  programs  have been build using Microsoft, Borland, and Watcom
  IDEs. Refer to IDE_INFO.DOC for more information on using specfic IDEs.


  3.7 Making the Library


  Registered  users  may  wish  to  assemble PCL4W.ASM.  Use the /MX switch in
  order to disable automatic conversion from lower case to upper case.  If the
  /MX switch is not used, then all PCL4W function references in C code must be
  in upper case. To assemble using the Microsoft assembler, use  the  provided
  makefile "PCL4W.MAK". From the DOS command line, type

       nmake pcl4w.mak

  Two  libraries  are  made, one with transmitter interrupts disabled (PCL4W1)
  and one with transmitter interrupts enabled (PCL4W2). Most users should  use
  the  library  without transmitter interrupts enabled since they require less
  overhead.

  To use the PCL4W qlibrary without transmitter interrupts enabled, type

       copy pcl4w1.lib pcl4w.lib
       copy pcl4w1.dll pcl4w.dll

  To use the PCL4W library with transmitter interrupts enabled, type

       copy pcl4w2.lib pcl4w.lib
       copy pcl4w2.dll pcl4w.dll

  After creating PCL4W.LIB and PCL4W.DLL, the example programs can be compiled
  and linked. Refer to Chapter 7.0, "Example Programs".














 PCL4W Users Manual                                                Page 12
  4.0 Talking to Your Modem


  A  modem  is  used  to  extend  the distance over which you may communicate.
  Without a modem, your RS232 cable is limited to a maximum  of  approximately
  50 feet.  But with a modem, you can communicate literally around the world.


  4.1 Modem Standards


  Two modems can communicate over a telephone line only if they are both using
  the  same  signaling frequencies and modulation, which are determined by the
  the modem standards used.  Modem standards can be divided into  three  sets:
  (1) speed, (2) data compression used, and (3) error control.

  The  Bell  standards  (103  &  212A)  are  those  of  AT&T.   The CCITT (The
  International Consultative Committee for Telephone and Telegraph)  standards
  are designated as "V. ".


  Speed


       Bell 103  :   300 baud
       Bell 212A :  1200 baud
       V.21      :   300 baud
       V.22bis   :  1200 & 2400 baud
       V.32      :  4800 & 9600 baud
       V.32bis   :  4800, 7200, 9600, 12000, and 14400 baud


  Data Compression


       MNP 5     :  Microcom Networking Protocol (proprietary).
       V.42bis   :  International data compression standard.


  Error Control


       MNP 2,3,4 :  Three level error correction (public domain).
       V.42      :  International error correction standard.























 PCL4W Users Manual                                                Page 13
  4.2 Flow Control


  With  modems  using data compression, the modem to modem connection will run
  at various speeds depending on the quality of the  line.   The  computer  to
  modem  connection  will be at a fixed baud rate. Therefore, a protocol (flow
  control) is necessary to synchronize the data flow between a modem  and  the
  computer  to  which  it  is  connected.   Refer  to  your  modem  manual for
  information on flow control protocols supported.

  Two flow control protocols are used by most all modems  which  require  flow
  control.  Software  flow  control  is called "XON/XOFF" (other software flow
  control character pairs are defined but operate the same  as  XON/XOFF)  and
  hardware  flow  control is called "RTS/CTS".  Most modems which require flow
  control enable hardware flow control by default.

  In XON/XOFF (software) flow control, the computer suspends transmitting data
  if it receives a XOFF character (13  hex)  from  the  modem,  and  continues
  transmitting  when  it  receives  a XON character (11 hex).  Similiarly, the
  computer can signal the modem not to send any more data  by  transmitting  a
  XOFF  to  it,  and  can tell the modem to continue transmission be sending a
  XON.

  In RTS/CTS (hardware) flow control, the RTS line is used by the computer  to
  signal  the  modem  ,  while the CTS line is used by the modem to signal the
  computer.  The RTS line is set OFF by the computer  to  tell  the  modem  to
  suspend  transmission,  and  set  to  ON  to  tell  the  modem  to  continue
  transmission.  The CTS line is set to OFF by the modem to tell the  computer
  to  stop  transmitting,  and  set  to  ON  to  tell the computer to continue
  transmitting.

  Given the choice, always choose hardware flow  control  over  software  flow
  control  so  that  all  data  transmission is transparent.  If hardware flow
  control is not the default (which it almost always is),  you  should  modify
  your modem initialization string to turn hardware flow control on.
































 PCL4W Users Manual                                                Page 14
  4.3 MODEM I/O (MIO)

  4.3.1 MIO Introduction

  The file MIO.H contains declarations for using the  Modem  I/O  DLL.   These
  functions  ease  communicating  with  modems  using  AT commands.  The LOGIN
  example program code has examples of using the MIO functions.

  The Windows "operating system" is what is called "cooperative multitasking".
  This  means  that  the  executing  Windows  task  must voluntarily "give up"
  control before another Windows task (or Windows itself) can execute.

  The difficulty  is  how  to  wait  for  a  number  of  seconds  while  still
  relinquishing control periodically before the wait is up. One solution is by
  making  functions that need to wait (such as the MIO functions) into "state"
  machines. A function is broken down into parts called states, and control is
  returned to Windows between executing each state.

  For example, to send the string "ATDT1,205,880,9748" to the modem  with  one
  tenth second delay between transmitted characters, the following sequence is
  used:

  (1) Send the string to the MIO driver by executing:

  Code = mioSendTo(Port,100,"!ATDT1,205,880,9748")

  The '!' characters are converted to carriage returns.  The  text  string  is
  copied into the driver's data area.

  (2)  Call mioDriver (typically based on a timer) until MIO_IDLE is returned.
  Each time mioDriver is called, it will send another character to  the  modem
  provided  the  required  delay  (since  the previous character was sent) has
  passed.  If the delay has not passed, the driver simply returns MIO_RUNNING,
  but without actually sending a character to the modem.  Once all  characters
  have been sent, mioDriver will return MIO_IDLE, indicating it is done and is
  ready to accept another function.

  mioDriver  will return MIO_RUNNING if it is still processing.  Anything else
  received indicates that it is still processing and the returned value  is  a
  character from the modem that can be displayed if wanted.

  (3) Once mioDriver returns MIO_IDLE, call mioResult to get the result of the
  mioSendTo call.

  The above is rather straight forward in practice.  See the LOGIN application
  for an example of its use.


  4.3.2 MIO Functions

  4.3.2.1 mioDriver

  Syntax: int mioDriver(int Port)

  mioDriver  executes  the  next  state of any previously started MIO function
  such as mioSendTo, mioWaitFor, and mioQuiet. It returns:

  MIO_IDLE    : if the driver is ready for the next mioSendTo, mioWaitFor, or
                mioQuiet.
  MIO_RUNNING : if the driver is not idle.
  <otherwise> : if the driver is not idle,  and  the  returned  character  was
                received from the modem.





 PCL4W Users Manual                                                Page 15
  4.3.2.2 mioBreak


  Forces the MIO driver to the IDLE state, abandoning any work in progress.


  4.3.2.3 mioSendTo


  Syntax:  int mioSendTo(int Port, long Pace, char *String)

  The mioSendTo function sends the characters in the string 'Text'  to  serial
  output. There is a delay of 'Pace' milliseconds between characters.


  4.3.2.4 mioWaitFor


  Syntax: int mioWaitFor(int Port, long Wait, int Case, char *String)

  The  mioWaitFor  function  waits for characters from serial input that match
  the string 'Text'. A total of 'Wait' milliseconds are allowed before  timing
  out  and  returning  FALSE (0).  If the 'Case' flag is TRUE, then the string
  comparison is NOT case sensitive.

  For example, to wait up to one minute for "CONNECT", "NO CARRIER", or "BUSY"
  from the modem after dialing a number (on COM1):

  Code = mioWaitFor(COM1,60000,1,"CONNECT|NO CARRIER|BUSY")

  The function mioDriver() must be called until MIO_IDLE  is  returned.   Then
  mioResult()  is  called  to  get the result of the mioWaitFor.  A value of 0
  indicates  that  neither "CONNECT", "BUSY", nor "NO CARRIER" was received. A
  non-zero value indicates that one of the three sub-strings was received.   A
  ASC("0")  is  returned  if  "CONNECT"  was seen, ASC("1") is returned if "NO
  CARRIER" was seen, and ASC("2") is returned if "BUSY" was seen.


  4.3.2.5 mioQuiet


  Syntax: int mioQuiet(int Port,long Wait)

  The mioQuiet function waits for continuous quiet [no incoming  serial  data]
  of  'Wait'  milliseconds  before  returning.   Any  incoming character while
  mioQuiet us running is flushed.


  4.3.3 MIO Summary


  mioDriver   : Allows  the  execution  of  mioSendTo,  mioWaitFor, or
                mioQuiet once they have been  started.  Returns  MIO_IDLE
                (defined in MIO.H) if ready not running,   MIO_RUNNING if
                running,  and anything else is a character from the modem
                that can be displayed if wanted.
  mioBreak    : Forces the MIO driver to IDLE state.
  mioSendTo   : Sends string (including control chars) to the modem.
  mioWaitFor  : Waits for a particular string from the modem, passing
                all else through.
  mioQuiet    : Waits for continuous quiet of specified duration.
  mioBreak    : Breaks further modem I/O activity.





 PCL4W Users Manual                                                Page 16
  4.4 Modem Initialization


  If your application uses a modem (as opposed to using a null  modem  cable),
  then  you should always send an initialization string to your modem if it is
  a programmable modem such as those made by  Hayes.   Communication  programs
  such as PROCOMM and TELIX always send such a string automatically as soon as
  they start up.

  The particular initialization string depends on the make of your modem.  For
  Hayes  and  Hayes  AT  command  set  compatible modems, the following string
  (followed by a carriage return) should work:

       AT E1 S7=60 S11=60 V1 X1 Q0 S0=0

  Refer to your Modem User's Guide for a full discussion of these commands.  A
  brief description is as follows:

       AT     Modem attention command.
       E1     Modem will echo what you send to it.
       S7=60  Wait 60 seconds for carrier and/or dial tone.
       S11=60 Use 60 milliseconds for tone dialing duration & spacing.
       V1     Display result code as words (not numbers).
       X1     Use the extended result message (CONNECT XXXX) set.
       Q0     Modem returns result codes.
       S0=0   Do not answer RING.

  If  your application will answer incoming calls, then set the S0 register to
  the ring on which to automatically answer.

  If you send the above codes by using SioPutc (as opposed to typing them from
  the keyboard), then follow these guidelines:

  (1) Send an initial carriage return before the initialization string.

  (2) Pause at least 150 milliseconds after each character sent as your  modem
  needs the time to perform its own internal processing. Pause a little longer
  if your modem is not accepting your initialization string.

  (3)  Pause  one  and a half seconds after sending any initialization command
  such as ATZ or AT&F since your modem must do quite a bit of processing.

  If you experience any problems in initializing your Hayes modem, you  should
  first reset it to factory settings by sending:

       AT&F

  Refer to the LOGIN program (function SendToModem in the file MODEM_IO.C)  for
  an example of sending an initialization string to a Hayes compatible modem.


















 PCL4W Users Manual                                                Page 17
  5.0 Problems


  If  you  cannot  get your application to run properly, first compile and run
  the terminal emulator program SIMPLE provided  on  your  distribution  disk.
  Test  SIMPLE  by  connecting  two  computers  with  a null modem cable or by
  commanding a Hayes AT command set compatible modem.

  Once  SIMPLE  runs, compile and run the SELFTEST program.  This program will
  test your serial ports functionality.

  If your application does not run but  SIMPLE  and  SELFTEST  run  correctly,
  then  you  have  most likely made a programming mistake in your application.
  MarshallSoft Computing cannot debug your application,  especially  over  the
  telephone!  However,  consider  each  of the following when searching for an
  error in your application.

  1.  Have you included the file PCL4W.H in your application ?

  2.  Is your receive buffer large enough ? If you are using 1K data blocks in
  YMODEM,  then  your  receive  buffer should be at least 1K (2K if baud rates
  above 19200 are to be used).

  3.  Have you selected too high a baud rate? Windows can multitask many tasks
  at once. You may have to lower your baud rate (or get 16550 UARTS).

  4.  If you are running two COM ports simultaneously, are you using separate
  receive and transmits buffers ? (you should).

  5.  Did SioReset return a zero value ?  If not, then you must call  SioReset
  again. See LOGIN.C for an example.

  6.   Did  you  send the proper initialization string to your modem ? Did you
  set DTR and RTS ? (you should).

  7.  Do you have more than one COM1 port?  For example, if you  have  a  COM1
  port  on  your  motherboard, you cannot add another COM1 port or modem board
  that uses COM1 without first disabling the COM1 on the motherboard.

  8.   Is  your  IRQ set correctly? If you can transmit data but can't receive
  using the PCL4W library with transmitter interrupts disabled (PCL4W2),  then
  this usually means that interrupts are not working.

  9. If -19 is returned from SioReset, this means that  you  have  not  called
  PostMainHandle() from within your code first. See example in SIMPLE.C.

  We recommend the following steps if you believe that you have  discovered  a
  bug  in  the  library:  (1)  Create  the  smallest,  simpliest  test program
  possible that demonstrates the problem.  (2)  Document  your  exact  machine
  configuration  and  what error the test program  demonstrates.   (3)  Upload
  the example source to our user support BBS, email it or mail us a disk.

  If  the  problem can be solved with an easy work-around, we will publish the
  work-around.  If the problem requires a modification to the library, we will
  make the change and make the modified library  available  to  our  customers
  without charge.











 PCL4W Users Manual                                                Page 18
  6.0 Serial Communications

  6.1 Communications Basics


  The  heart  of  serial  communications  is  the UART (Universal Asynchronous
  Receiver Transmitter).  The IBM  PC/XT/AT  and  compatibles  use  the  8250,
  16450, or the 16550 UART.  The purpose of the UART is:

  (1) To convert bytes from the CPU (Central Processing Unit), into  a  serial
  format  by  adding  the  necessary start, stop, and parity bits to each byte
  before transmission, and to then transmit each bit at the correct baud rate.

  (2) To convert the incoming stream (at a specified baud rate) of serial bits
  into bytes by removing the start, stop, and parity bits  before  being  made
  available to the CPU.

  The  UART  is part of the serial interface circuitry which allows the CPU to
  send and receive signals over the RS232 lines. This  can  be  diagrammed  as
  follows:



                        Serial Interface
                     +-------------------+
                     |                   |
  +-----+  Data Bus  |     +------+      |    RS232 Signals
  | CPU +------------+     | UART |      +----------------*
  +-----+            |     +------+      |
                     |                   |
                     +-------------------+



  The  8250/16450/16550  UART  is  capable  of  operating in one of two modes,
  "polled" and "interrupt driven".  The serial communications functions in the
  BIOS uses the polled method.  In this approach, the CPU is  typically  in  a
  loop  asking  the  UART  over  and over again if it has a byte ready. If its
  does, the polling code returns the byte.  But, if the  next  byte  comes  in
  before the polling code is executing again, then that byte is lost.

  In the interrupt driven approach (used by PCL4W), when a byte is received by
  the  UART,  an  "Interrupt  Service  Routine" (ISR) is executed immediately,
  suspending temporarily whatever else is executing. The ISR  then  moves  the
  byte to a buffer so that your application program can later read it.

  If transmitter interrupts are enabled, then  bytes  are  queued  up  waiting
  transmission.   When  a  byte  is  moved  from  the UART transmitter holding
  register to the UART transmitter shift register, an interrupt  is  generated
  and  the  next  byte is taken from the library transmitter buffer by the ISR
  and written to the UART holding register.

  Up to 16 bytes can be taken from the transmitter buffer while processing one
  transmitter  interrupt  if an 16550 UART is used. The 16550 UART is strongly
  recommended for computers doing serial communications under Windows.

  Refer to Sections  6.6  and  6.7  entitled  "RS232  Signals"  and  "National
  INS8250,   INS16450,   and   INS16550   UARTs",   respectively  for  further
  information on these topics.








 PCL4W Users Manual                                                Page 19
  6.2 Standard Port Addresses


  There  are  a  few  things to know about how serial communications ports are
  used by IBM PC/XT/AT and compatible computers.  The  standard  IBM  PC/XT/AT
  configuration values are as follows:

        Port     Reg Base   IRQ Line   Vector
        COM1        3F8H         4        12
        COM2        2F8H         3        11
        COM3        3E8H         4        12
        COM4        2E8H         3        11

  (Refer  to  your  DigiBoard  manual  for  DigiBoard addresses, and your BOCA
  manual for BOCA board addresses).

  PCL4W  assumes the above values.  If necessary, the UART base address can be
  changed by SioUART, and IRQ lines can be re-assigned  by  SioIRQ.   Remember
  that  each  port to be used concurrently must have a unique IRQ line.  Refer
  to the PCL4W Reference Manual for specific details.

  When installing new  communications  cards,  the  following  guidelines  are
  recommended:

  (1)  Be  sure to read the documentation for the hardware you are installing.
  Pay special attention to UART base addresses and IRQ lines, particularly  if
  trying to set up a non-standard configuration.

  (2)  If  you  have  a  choice in base addresses and IRQ lines, always choose
  standard values as defined above.

  (3) The first port should be COM1, the second COM2, etc.

  (4)  Use SioUART to zero all unused ports (for example, call SioUART(COM4,0)
  if there is no COM4 port installed).

  (5) Be carefull not to configure two ports for the  same  address.  This  is
  easier to do than you may believe.

  (6)  Choose  an  external  modem over an internal one.  It is much easier to
  debug problems with an external modem than an internal one.

  (7) Select hardware flow control (RTS/CTS) if flow control is  required  and
  hardware flow control is not the default.

  (8)  Always  test your port as soon as it is installed. Try several programs
  that use the communications ports.




















 PCL4W Users Manual                                                Page 20
  6.3 Running 3 or 4 Ports Concurrently


  PCL4W supports up to 4 serial ports running concurrently (more if you have a
  DigiBoard or BOCA board).  One free interrupt for  each  port  is  required.
  Refer to the next section if you have a DigiBoard or BOCA board.

  Interrupts IRQ4 and IRQ3 are dedicated to  the  communications  ports  in  a
  standard  IBM  PC/XT/AT configuration.  IRQ4 is shared between COM1 and COM3
  while IRQ3 is shared between COM2 and COM4.  This means that you can run two
  ports simultaneously provided that they don't share an interrupt.

  Suppose that you wish to run 3 ports simultaneously. To begin, you must have
  3 serial UARTs installed on your computer.  Assume,  for  purposes  of  this
  discussion,  that  COM1  is installed on your motherboard, and that you have
  purchased a new 2 port serial communications board.

  You should be able to configure the first serial board port as  COM2,  which
  uses IRQ3.  Refer to the manual that came with your serial board.

  In  order  to  run the third serial port concurrently with the first two, an
  unused interrupt must be found.  If your serial card can use only  IRQ3  and
  IRQ4,  then there is no way to run a third line since IRQ4 and IRQ3 are used
  for COM1 and COM2.

  However, many serial cards can use other IRQs, typically IRQ2 through  IRQ7.
  Since  IRQ5  is  normally  used  for  a  second  printer  port, it is a good
  candidate for COM3. To use IRQ5 for the third serial port,  first  set  your
  serial card to use IRQ5 for COM3 (refer to your serial card manual) and then
  add the following line to your applications code before calling SioReset:

       SioIRQ(COM3,IRQ5);

  Don't  forget  to  disable  any device that might use IRQ5, such as a second
  printer port or a music card.   Unfortunately,  there  is  no  easy  way  to
  determine  that  you have no conflicts until you actually attempt to use the
  IRQ. If there are conflicts, your system will probably  hang  and  you  will
  have to reboot.

  To  run  a  fourth  serial  port,  another  free IRQ must be found.  On some
  systems, IRQ7 can be used. You must first disable IRQ7 on your parallel port
  card first (your printer doesn't need an IRQ). To use IRQ7  for  the  fourth
  serial port, first set your serial card to use IRQ7 for COM4 and then add:

       SioIRQ(COM4,IRQ7);

  To  summarize,  your  serial  card must be able to generate the correct IRQ,
  which is not already being used. Refer to the entry for the SioIRQ  function
  in the PCL4W Reference Manual.


















 PCL4W Users Manual                                                Page 21
  6.4 Using Multiport Cards


  The  PCL4W  library supports the dumb Digiboard (PC/4 and PC/8) and the dumb
  BOCA board (BB1004, BB1008, and BB2016).   Most  multiport  boards  will  be
  compatible  with either the DigiBoard (the status register contains the port
  number), or the BOCA board (the status register is bit mapped).

  6.4.1 The DigiBoard

  In order to use the DigiBoard, (not the Intelligent Digiboards such  as  the
  PC/Xe  and  PC/Xi) you must configure PCL4W using the SioPorts(), SioUART(),
  and SioIRQ() functions.

  Your  PCs  ports  must be partitioned into "standard" PC ports and dumb card
  ports.  Remember that standard PC ports cannot share IRQs like the DigiBoard
  (or BOCA board) can. If you are using IRQ4 and IRQ3 for  standard  PC  ports
  COM1  and  COM2, then you cannot use either for DigiBoard ports (try IRQ5 or
  IRQ7).

  Suppose that COM1 through COM2 are standard PC ports (using IRQ4  and  IRQ3)
  and  you  have  installed  a  PC/8  DigiBoard  that you wish to use for COM3
  through COM10 using interrupt line IRQ5.  You choose to use the  recommended
  DigiBoard UART addresses starting at 0x100:

     SioPorts(10,COM3,0x140,DIGIBOARD);/* COM3 = 1st DigiBoard port */
     Address  = 0x100;                 /* 1st DigiBoard UART address */
     for(Port=COM3;Port<=COM10;Port++) /* look at each port    */
       {SioUART(Port,Address);         /* set the UART address */
        Address += 8;                  /* compute next address */
        SioIRQ(Port,IRQ5);             /* set the DigiBoard IRQ */
       }

  The DigiBoard uses 0x140 for the status address for odd interrupts and 0x141
  for even interrupts.

  Digiboard  may  be  contacted  at  6400 Flying Cloud Drive, Eden Prairie, MN
  55344.  Telephone 612-943-9020 or FAX 612-943-5398.


  6.4.2 The BOCA Board

  In  order  to  use  the dumb BOCA Boards, you must configure PCL4W using the
  SioPorts(), SioUART(), and SioIRQ() functions.

  For example, to configure the BOCA BB2016 to use COM1 to  COM16,  with  base
  addresses starting at 0x100 and IRQ5:

     SioPorts(16,COM1,0x107,BOCABOARD);/* COM3 = 1st BOCA board port */
     Address = 0x100;                  /* 1st BOCA UART address */
     for(Port=COM1;Port<=COM16;Port++) /* look at each port    */
       {SioUART(Port,Address);         /* set the UART address */
        Address += 8;                  /* compute next address */
        SioIRQ(Port,IRQ5);             /* set the BOCA IRQ */
       }

  BOCA may be contacted at BOCA Research, Inc., 6413  Congress  Avenue,  Suite
  130, Boca Raton, FL 33487.  Phone 407-241-8088, FAX 407-997-0918.









 PCL4W Users Manual                                                Page 22
  6.5 Transmitter Interrupts


  Transmitter interrupts are supported by the library.  Separate libraries are
  provided, one with transmitter interrupts enabled  and  one  without.   When
  transmitter  interrupts  are  NOT  enabled, the following logic occurs every
  time you call SioPutc():

   1. Wait for transmit buffer to become empty. The transmit  buffer  may  not
  be empty if the previous transmit is not completed (the UART breaks down the
  byte  &  sends  1  bit at a time). 2. When the transmit buffer is empty, the
  byte from the SioPutc() call is loaded into the transmit buffer and  control
  is returned to the caller.

  Note that you can not write to the UART any faster the the UART baud rate.

  When transmitter interrupts are enabled, the byte from SioPutc() is put into
  a previously prepared (by SioTxQue) transmitter queue. The interrupt service
  routine fetches bytes from this queue as soon as the previous byte has  been
  sent.

  While you can now call SioPutc() faster than the baud rate, bytes are  still
  transmitted at the given baud rate.

  The   above   sounds   like  transmitter  interrupts  are  the  way  to  go.
  Unfortunately, this is usually NOT the case.  Most applications will perform
  better if transmitter interrupts are NOT enabled.

  The reason is that transmitter interrupts double the amount of code  in  the
  time  critical interrupt service routine.  While the library is processing a
  transmitter interrupt (which can take a while), incoming bytes  can  not  be
  processed.  What this means is that a given machine can run at a higher baud
  rate without transmitter interrupts. This problem is compounded when running
  multiple ports simultaniously.

  However,  there are a few application areas where transmitter interrupts are
  preferable.  If your application will be  transmitting  blocks  of  data  at
  fairly slow baud rates you might profit from enabling transmitter interrupts
  provided  that there is something else for the processor to do (which is NOT
  the case in most protocols).

  However,  if  you are using 16550 UARTS (which have 16 byte on-chip transmit
  and receive buffers rather that the 1 byte buffers on  the  8250  and  16450
  UARTS),  you  may  want  to  use the library version with interrupts enabled
  provided that you enable the 16550 UART with the SioFIFO() function.






















 PCL4W Users Manual                                                Page 23
  6.6 RS-232 Signals


  RS-232 is the name of the serial data interface  standard  used  to  connect
  computers  to modems.  Most IBM compatible computers are built with at least
  one serial port and use either DB9 (9 pin) or DB25 (25 pin) connectors.

  A summary of these pins and  their  function  follows.   For  more  detailed
  information, refer to one of the many books dealing with RS-232 interfacing.

  Signal Ground Pin 7 (DB25), Pin 5 (DB9)

  The  SG  line  is  used  as  the  common  signal  ground, and must always be
  connected.

  Transmit Data Pin 2 (DB25), Pin 3 (DB9)

  The TX line is used to carry data from the computer to the modem.

  Receive Data Pin 3 (DB25), Pin 2 (DB9)

  The RX line is used to carry data from the modem to the computer.

  Data Terminal Ready Pin 20 (DB25), Pin 4 (DB9)

  The DTR line is used by the computer to signal the modem that it  is  ready.
  DTR should be set high when talking to a modem.

  Data Set Ready Pin 6 (DB25), Pin 6 (DB9)

  The DSR line is used by the modem to signal the computer that it is ready.

  Request to Send Pin 4 (DB25), Pin 7 (DB9)

  The  RTS  line  is used to "turn the line around" in half duplex modems, and
  for hardware flow control in most modems that require flow control.  RTS  is
  controlled by the computer and read by the serial device (modem).

  Clear to Send Pin 5 (DB25), Pin 8 (DB9)

  The  CTS  line  is used to "turn the line around" in half duplex modems, and
  for hardware flow control in most modems that require flow control.  CTS  is
  controlled by the serial device (modem) and read by the computer.

  Data Carrier Detect Pin 8 (DB25), Pin 1 (DB9)

  The DCD line is used by the modem to signal the computer that a data carrier
  signal is present.

  Ring Indicator Pin 22 (DB25), Pin 9 (DB9)

  The RI line is asserted when a 'ring' occurs.















 PCL4W Users Manual                                                Page 24
  6.7 National INS8250, INS16450, and INS16550 UARTs


  The  Personal  Communications  Library  is  based  on  the standard National
  INS8250, INS16450, and INS16550 UARTs. The 8250 was the original  UART  used
  in  the IBM PC, whereas the 16450 is a faster version found on most 286 & up
  machines. The 16550 contains a 16 byte FIFO to further reduce communications
  overhead. These UARTs consists of 8 register ports as follows:

  Offset R/W Register
     0   R/W    Receiver  (read)  /  Transmitter  (write)
     1   R/W    Interrupt Enable (read)
     2   R      Interrupt Identification
     2   W      FIFO control (INS16550 only)
     3   R/W    Data Format (Line Control)
     4   R/W    RS-232 (Modem) Control
     5   R/W    Line Status
     6   R/W    RS-232 (Modem) Status
     7   R/W    Not used.

  For  the  standard  PC  ports  (not DigiBoard ports), the UART registers are
  based at 3F8h (COM1), 2F8h (COM2), 3E8h (COM3), and 2E8h (COM4).   COM1  and
  COM3  share  interrupt  request  line IRQ4 while COM2 and COM4 share request
  line IRQ3.  This means that  COM1  and  COM3  can't  be  used  concurrently.
  Similarly for COM2 and COM4.

  However,  standard PC ports may be re-configured to use other UART addresses
  and IRQ assignments.  Refer  to  the  SioPorts(),  SioUART(),  and  SioIRQ()
  functions.

  If  you  have  a  DigiBoard PC/4 (or PC/8) installed, you will have 4 (or 8)
  additional ports using INS16450 or INS16550 UARTS.   The  default  DigiBoard
  ports  are  located  at 100h, 108h, 110h & 118h for the PC/4 continuing with
  120h 128h, 130h & 138h for the PC/8. IRQ3 is the default for all ports.

  Four sources of interrupts  are  possible  with  the  8250  and  16550:  (1)
  receiver error or BREAK, (2) receiver data ready, (3) ready to transmit, and
  (4)  RS232  input.   These  four  sources  of  interrupts  are summarized as
  follows:

       Source of Interrupt        Action Required to Clear
       Receiver error or BREAK.   Read Line Status register.
       Receiver data.             Read data from data register.
       Transmitter Buffer Empty.  Write to data register or read IID reg.
       RS232 Input.               Read Modem Status register.

  If  you are not familiar with UARTS, several good books are available. Refer
  to  Chapter  6.0,  Serial  Communications   chapter   for   recommendations.
  Although  a knowledge of the 8250/16450/16550 is not necessary to use PCL4W,
  a general knowledge of the theory of asynchronous serial  communications  is
  helpful.
















 PCL4W Users Manual                                                Page 25
  6.8 Register Summary


  REG 0 : Data Register

  Reading from the data register fetches the  next  input  byte,  once  it  is
  ready.   Writing  to the data register transmits the byte written to it over
  the serial line.

  REG 1 : Interrupt Enable 

  The Interrupt Enable register enables each of four types of interrupts  when
  the appropriate bit is set to a one.

       bit 3 :  Enable interrupt  on  RS232  input.
       bit 2 :  Enable interrupt on receiver error or break.
       bit 1 :  Enable interrupt on transmitter buffer empty (TBE).
       bit 0 :  Enable interrupt on received data (RxRDY).

  REG 2 : Interrupt Identification (IID)

  Reading the Interrupt Identification (read only) register once an  interrupt
  has occurred identifies the interrupt as follows:

       Bit 2  Bit 1  Bit 0  Priority   Interrupt
         0     0      1      none      none
         1     1      0      0         (high) Serialization or break.
         1     0      0      1         Received data.
         0     1      0      2         Transmitter Buffer Empty.
         0     0      0      3         (low) RS232 Input.

  In  the  INS16650,  REG  2  (write  only) is also the FIFO control register.
  Writing bits 6 & 7 will set the FIFO trigger level (number of bytes received
  before an interrupt is generated).

        Bit 7  Bit 6   Trigger             Bit 7  Bit 6   Trigger
          0      0      1 byte               1      0     8 bytes
          0      1      4 bytes              1      1     14 bytes

  REG 3 : Line Control

  RS232 line parameters are selected by writing to this register.

       bit 7   : DLAB = 0
       bit 6   : BREAK on(1), off(0).
       bits 5-3: Parity None(000),ODD(001),EVEN(011),MARK(101),SPACE(111)
       bit 2   : One stop bit(0), two stop bits(1).
       bits 1-0: Data bits = 5 (00), 6(01), 7(10), 8(11).

  When  the Divisor Latch Access Bit (DLAB) is 1, registers 0 and 1 become the
  LS and MS bytes of the Baud Rate Divisor registers.

       Baud   Divisor      Baud  Divisor      Baud  Divisor
        300    0180        4800   0018       38400   0003
       1200    0060        9600   000C       57600   0002
       2400    0030       19200   0006      115200   0001











 PCL4W Users Manual                                                Page 26
  REG 4 : Modem Control

  RTS, DTR, loopback testing, and  General  Purpose  Outputs  #1  and  #2  are
  controlled by the Modem Control register as follows:

       bit 4 : Enable local loopback.
       bit 3 : Enable GP02. Necessary for 8250 interrupts.
       bit 2 : Enable GP01.
       bit 1 : Set / clear RTS.
       bit 0 : Set / clear DTR.

  REG 5 : Line Status

  Reading  the  Line Status register provides status information as follows (1
  for TRUE, 0 for FALSE) :

       bit 6 : Transmitter Empty.
       bit 5 : Transmitter Buffer Empty (TBE).
       bit 4 : BREAK detect.
       bit 3 : Framing error.
       bit 2 : Parity error.
       bit 1 : Overrun error.
       bit 0 : Data Ready.

  REG 6 : Modem Status

  Reading the Modem Status register provides the following status  information
  (1 for TRUE, 0 for FALSE) :

       bit 7 : DCD status.
       bit 6 : RI status.
       bit 5 : DSR status.
       bit 4 : CTS status.
       bit 3 : Delta DCD status.
       bit 2 : Delta RI status.
       bit 1 : Delta DSR status.
       bit 0 : Delta CTS status.

  The delta bits (bits 0 through 3) are set whenever one of  the  status  bits
  (bits  4 through 7) changes (from 0 to 1 or from 1 to 0) since the last time
  the Modem Status register was read. Reading the Modem Status register clears
  the delta bits.

  REG 7 : Scratch Register

  There  is  no  function  associated  with  register 7.  It does not exist in
  earlier versions of the 8250.




















 PCL4W Users Manual                                                Page 27
  7.0 Example Programs


  The  example programs can be built either using the command line makefile or
  directly from your compiler's IDE (see section 3.6 "Using and IDE").


  7.1 SIMPLE

  SIMPLE  is a very simple communications programming using PCL4W.  Everything
  that is typed on the keyboard is sent to  the  serial  port,  and  everthing
  incoming from the serial port is displayed on the screen.

     Using the Microsoft command line compiler: NMAKE SIMPLE._M_
     Using the Borland command line compiler:   MAKER -fSIMPLE._B_
     Using the Watcom command line compiler:    WMAKE -f SIMPLE._W_

  If you are using  the  Borland  IDE,  be  sure  and  turn  off  LINKER  case
  sensitivies:  Choose  OPTIONS,  PROJECTS,  LINKER,  GENERAL and turn off the
  "case sensitive link" and "case sensitive exports & imports" boxes.

  The SIMPLE makefiles use the small memory model. If a different memory model
  is  required,  the  Microsoft  (or  Borland)  runtime  library  must also be
  changed to match the memory model. No  change  is  required  for  the  PCL4W
  library.

  For example, to change the makefile from using the  small  memory  model  to
  using  the  medium  memory  model,  the following changes are necessary: For
  Microsoft, change -AS to -AM and change SLIBCEW to  MLIBCEW.   For  Borland,
  change -sm to -mm and change C0WS, CWS, and MATHWS to C0WM, CWM, and MATHWM.

  7.2 LOGIN

  LOGIN  is the same program as SIMPLE but with the addition of "Modem" on the
  menu bar.  Under "Modem", select "Start", then "Handshake" in order to  send
  an "AT" to the connected modem, or "Dial" to send a dial string to the modem
  (which  dials  our  user  support  BBS). Once the dial sequence is sent, the
  program will wait for up to 60 seconds for the  "CONNECT"  string  from  the
  modem.  This  wait  can  be terminated at any time by choosing "BREAK" under
  "Modem".

  To  test LOGIN, you need a AT command set compatible modem and a BBS to call
  up. LOGIN will dial our BBS at 205-880-9748, or  edit  the  dial  string  in
  LINE.C to call up a local BBS.

  7.3 SELFTEST

  SELFTEST performs a serial port I/O functionality test. A single port can be
  tested  if  a  loopback adapter is connected to the end of the serial cable.
  Refer to LOOPBACK.DOC for an explanation of how to make a loopback adapter.

  7.4 TERM


  TERM  is  an  example  communications  program suitable for calling bulletin
  board systems (BBS).

  TERM features modem initialization, hardware flow control, and state  driven
  file  transfer  using  ASCII,  XMODEM, and YMODEM, communications protocols.
  TERM can be used to  call  up  any  bulletin  board  system,  including  the
  MarshallSoft Computing BBS.

  In  an  attempt  to  minimize the size of the shareware version of the PCL4W
  library,  the  TERM  program  files  are  distributed  as  a  separate  file
  (WTERMxx.ZIP,  where  xx  is the current version). WTERMxx.ZIP can always be
  downloaded from the MarshallSoft support BBS.

 PCL4W Users Manual                                                Page 28
  8.0 Legal Issues

  8.1 Registration


  If you wish to register the PCL4W library, please send $75 plus $5 S&H  ($10
  outside of North America) to:

       MarshallSoft Computing, Inc.
       Post Office Box  4543
       Huntsville AL 35815-4543

  Multiple  copies  are  available: $60 each for 2 to 5, $45 each for 5 to 10,
  and $30 each for 20 or more.  A site license  is  also  available  for  $495
  (includes 5 sets of printed documentation). We pay shipping.

  We accept American Express, VISA, MasterCard, checks in US dollars drawn  on
  a   US   bank, International Postal Money Orders, purchase orders (POs) from
  recognized US schools and companies listed in  Dun  &  Bradstreet,  and  COD
  (street  address and phone number required) within the USA (plus a $4.50 COD
  charge).

  For  credit  card  orders,  be  sure  to  include  the  account  number, the
  expiration date, the exact name on the card, and the complete  card  billing
  address (the address to which the credit card bill is mailed).

  You can also order PCL4W from The Public Software Library  (PSL)  with  your
  MC,  Visa,  AmEx,  or  Discover card by calling 800-242-4PSL (from overseas:
  713-524-6394) or by FAX at 713-524-6398.  THESE  NUMBERS  ARE  FOR  ORDERING
  ONLY. The product number for PCL4W is 11171.

  Print the file PCL4W.INV if an invoice is needed.

  If you wish to update from an older version of PCL4W, send $25 plus  $5  S&H
  ($10  outside  of  North  America).   Updates  must be ordered directly from
  MarshallSoft Computing.

  The registered package includes:

       o  PCL4W Library w/o shareware screens.
       o  Assembler source code for the library.
       o  SCRIPT language V2.1 (compiler and interpreter).
       o  Laser printed Users and Reference Manuals.
       o  Telephone, BBS, and email support for one year.

  The  registered  user will receive the latest version of PCL4W shipped by US
  second day priority mail (packet airmail  overseas).   A  3.5"  diskette  is
  provided unless a 5.25" diskette is requested.

  All  prices  are guaranteed for one year from the release date as printed on
  the title page.
















 PCL4W Users Manual                                                Page 29
  8.2 License


  MarshallSoft  Computing,  Inc. grants the registered user of PCL4W the right
  to use one copy of the PCL4W library (in object form) on a  single  computer
  in  the  development  of  any software product (other than libraries such as
  PCL4W).  The user may not use the library on more than one computer  at  the
  same  time.   The  source code for the library (PCL4W.ASM) is copyrighted by
  MarshallSoft Computing and may not be released in whole or in part. Products
  developed using PCL4W may be distributed without any royalty.


  8.3 Warranty


  MARSHALLSOFT COMPUTING, INC.  DISCLAIMS  ALL  WARRANTIES  RELATING  TO  THIS
  SOFTWARE,  WHETHER  EXPRESSED  OR  IMPLIED, INCLUDING BUT NOT LIMITED TO ANY
  IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR  PURPOSE,
  AND  ALL  SUCH WARRANTIES ARE EXPRESSLY AND SPECIFICALLY DISCLAIMED. NEITHER
  MARSHALLSOFT COMPUTING, INC. NOR ANYONE ELSE WHO HAS BEEN  INVOLVED  IN  THE
  CREATION,  PRODUCTION,  OR DELIVERY OF THIS SOFTWARE SHALL BE LIABLE FOR ANY
  INDIRECT, CONSEQUENTIAL, OR INCIDENTAL DAMAGES ARISING OUT  OF  THE  USE  OR
  INABILITY  TO  USE  SUCH  SOFTWARE EVEN IF MARSHALLSOFT COMPUTING, INC.  HAS
  BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES OR CLAIMS. IN NO EVENT SHALL
  MARSHALLSOFT COMPUTING, INC.'S LIABILITY FOR ANY SUCH  DAMAGES  EVER  EXCEED
  THE  PRICE  PAID FOR THE LICENSE TO USE THE SOFTWARE, REGARDLESS OF THE FORM
  OF THE CLAIM. THE PERSON USING THE SOFTWARE BEARS ALL RISK AS TO THE QUALITY
  AND PERFORMANCE OF THE SOFTWARE.

  Some states do not allow  the  exclusion  of  the  limit  of  liability  for
  consequential  or  incidental damages, so the above limitation may not apply
  to you.

  This agreement shall be governed by the laws of the  State  of  Alabama  and
  shall  inure  to  the  benefit  of  Marshallsoft  Computing,  Inc.   and any
  successors, administrators, heirs and  assigns.  Any  action  or  proceeding
  brought  by either party against the other arising out of or related to this
  agreement shall be brought only in a STATE or  FEDERAL  COURT  of  competent
  jurisdiction  located in Madison County, Alabama. The parties hereby consent
  to in personam jurisdiction of said courts.



























 PCL4W Users Manual                                                Page 30
  9.0 Summary


  9.1 Revision History


  Version 1.0: 1 February, 1994.


  The  initial  release  of  PCL4W uses a considerable amount of the code from
  version 4.0 of PCL4C (the DOS version of the comm library).


  Version 1.1:  August 1, 1994


  o A flow control bug was fixed.
  o COM11 through COM16 defined.
  o Supports the BB1004, BB1008, and BB2016 BOCA boards.
  o The new function SioGetDiv() was added.
  o A script compiler & interpreter was added to the registration package.


  Version 1.2:  August 8, 1995


  o Defined ports extended to 20.
  o Support for all IRQs [IRQ0 to IRQ15].
  o Bug in BREAK detection corrected.
  o Bug in SioRxClear fixed.
  o SioInfo also returns # interrupts.


  Version 1.3: July 8, 1996

  o SioRxFlush renamed SioRxClear.
  o SioTxFlush renamed SioTxFlush.
  o Added more choices in SioInfo.
  o Added LOGIN & SELFTEST example programs.
  o Simplified SIMPLE example program.



























 PCL4W Users Manual                                                Page 31
  9.2 Function Summary

  Refer  to the PCL4W Reference Manual (PCL4W.REF) for detailed information on
  the communications and  support  functions.  A  one  line  summary  of  each
  function follows:

  +--------------+-----------------------------------------------------------+
  |  SioBaud     |  Sets the baud rate of the selected port.                 |
  |  SioBrkSig   |  Asserts, cancels, or detects BREAK signal.               |
  |  SioCTS      |  Reads the Clear to Send (CTS) modem status bit.          |
  |  SioDCD      |  Reads the Data Carrier Detect (DCD) modem status bit.    |
  |  SioDone     |  Terminates further serial processing.                    |
  |  SioDSR      |  Reads the Data Set Ready (DSR) modem status bit.         |
  |  SioDTR      |  Set, clear, or read the Data Terminal Ready (DTR) bit.   |
  |  SioFIFO     |  Sets the interrupt level for the INS16550.               |
  |  SioFlow     |  Enables / disables hardware flow control.                |
  |  SioGetc     |  Reads the next character from the serial line.           |
  |  SioGetDiv   |  Gets the baud rate divisor.                              |
  |  SioInfo     |  Returns library ver number, memory model, # interrupts   |
  |  SioIRQ      |  Assigns an IRQ line to a port.                           |
  |  SioLine     |  Reads the line status register.                          |
  |  SioLoopBack |  Performs a UART loopback test.                           |
  |  SioModem    |  Reads the modem status register.                         |
  |  SioParms    |  Sets parity, stop bits, and word length.                 |
  |  SioPorts    |  Sets # ports, 1st DigiBoard port & status register.      |
  |  SioPutc     |  Transmit a character over a serial line.                 |
  |  SioRead     |  Reads any of 7 UART ports.                               |
  |  SioReset    |  Initialize a serial port for processing.                 |
  |  SioRI       |  Reads the Ring Indicator (RI) modem status bit.          |
  |  SioRTS      |  Sets, clears, or reads the Request to Send (RTS) line.   |
  |  SioRxBuf    |  Sets up receive buffer.                                  |
  |  SioRxClear  |  Clears the receive buffer.                               |
  |  SioRxQue    |  Returns the number of characters in the receive queue.   |
  |  SioTxBuf    |  Sets up transmit buffer.                                 |
  |  SioTxClear  |  Clears the transmit buffer.                              |
  |  SioTxQue    |  Returns the number of characters in the transmit queue.  |
  |  SioUART     |  Sets the UART base address.                              |
  |  SioUnGetc   |  "Un-gets" (puts back) a specified character.             |
  +--------------+-----+-----------------------------------------------------+




























 PCL4W Users Manual                                                Page 32
  9.3 Further Reading


  The  best way to learn about serial communications is to read a good book on
  the subject. Several good texts are available.  Two that I like are:

  (1) C Programmers's Guide to Serial Communications by  Joe  Campbell  (SAMS)
  (2) Mastering Serial Communications by Peter Gofton (SYBEX).


  10.0 Other MarshallSoft Computing Products


  The following shareware  libraries  are  also  available  from  MarshallSoft
  Computing.   They  can  be  registered  directly  through us.

  10.1 The Personal Communications Library for C/C++

  The Personal Communications Library for the C  Language  (PCL4C)  is  a  DOS
  based  asynchronous communications library designed for experienced software
  developers programming  in  C.   Four  compilers  are  supported:  Microsoft
  Optimizing  C,  Microsoft Quick C, Borland Turbo C, and MIX Power C.  An IBM
  PC/XT/AT or compatible is required.  PCL4C is the DOS equivalent of PCL4W.

  The Personal Communications Library for C (PCL4C) is available for $75  plus
  $5  S&H ($10 S&H overseas). PCL4C and PCL4W can be ordered together for $120
  plus $5 S&H ($10 overseas).

  10.2 Libraries for Other Languages

  We  also have communications libraries for Turbo Pascal, Visual Basic (DOS),
  and PowerBASIC.  A Visual BASIC library for Windows is also available.



































 PCL4W Users Manual                                                Page 33