FSFS manufactured Douglas B-26C Invader.  Designed by Bill 
Cline with much appreciated help and work by Rush Mueller.
                ***************

"Model 7A...Model 7B...A-20 Havoc...A-26...A-26B Invader
...B-26 Invader."

Thus, we have the essential evolution of one of the 
classic aircraft spawned by World War II.

The designation A-26 was officially changed to B-26 in 
1947.  The Invader is often confused with the Martin B26 
Marauder.  Two completely different aircraft, of course.

The Invader was designed originally to be a night fighter 
but that designation was cancelled early because it 
offered no significant improvement over the Northrop P-61 
Black Widow, which was undergoing concurrent flight 
testing.

The B-26 evolved, therefore, into a heavily armed light 
attack bomber and was used in a wide variety of missions, 
including high, medium, and low altitude bombing, strafing, 
night and day ground support interdiction missions 
(WWII & Korea), night reconnaissance, photo, electronic 
recon and jamming, counter-insurgency (Vietnam), fire 
fighting, target towing, drone controlling, etc.


Specifications:

Wingspan................70' (21.34m)
Length..................50'8" (15.44m)
Height..................18'6" (5.64m)
Empty Weight............22,362 pounds(10,143kg)
Maximum Weight..........41,800 pounds(18,960kg)
Powerplants.............Two 2,100 hp Pratt & Whitney
                        R-2800 radial engines.

Armament................6,000 pound bomb load and
                        sixteen to eighteen .50 cal
                        machine guns.

Performance
  Maximum Speed.........518kph (450mph)
  Service Ceiling.......24,500 feet (7,470m)
  Range.................2,914 miles (4,690m)
Crew....................Three (pilot, bombardier, gunner)

Standard armament was either a six or eight gun nose, plus 
rear upper and lower turrets.  There were nose variations, 
however, mixing .50 caliber guns with 37MM and 75MM 
cannons.  There were also "glass noses" for navigator
/bombardier activities.  Thus, you could very easily use 
FSFS to design eight different noses to fit interchangably 
on your "stock" B-26!

The paint jobs are also varied.  This C Model Invader 
wears the colors of the 63rd TRW, 9th Air Force, Tactical
Air Command, USAF, circa 1955.

              *********************

Files and Installation:

  B26_C.0AF
  B26_C.1AF
  B26_C.2AF
  B26_C.AFX
  B26_C.AIR
  INVADER.DOC
  B26_C.LST
  CHECK1.PCX
  FUSE2.PCX
  RADIAL.PCX
  RADIAL.R8
  FUSE2.R8
  CHECK1.R8

  Copy *.AIR file to your \FLTSIM5\PILOTS subdirectory.
  Copy *.PCX, *.R8, and *.?AF files to your FLTSIM5\TEXTURE  
  subdirectory.

           **********************

FLIGHT CHARACTERISTICS AND SUGGESTED PROCEDURES.

The B-26 is a beauty to fly.  Fast, nimble, and 
responsive, most pilots liken it to a twin engined 
fighter.  As a matter of fact, the Dash 1 (Pilot's Manual) 
describes it as a Fighter/Bomber.  Though it was never the 
widow-maker that the original Martin B-26 was, it does not 
forgive improper handling, especially on landing!  Take, 
for example, a cousin of the B-26, the B-25.  The 
venerable and forgiving Mitchell can be rounded-out 
several feet in the air, and will quietly mush on down to 
a comfortable touchdown, whereas the Invader needs to be 
flown right down to the runway with the nose wheel just 
inches off the ground.  We used to call it the 3 inch 
flare.  The book says, "fly it into the ground".  You do 
have to be sure your vertical speed at touchdown is 
reasonably low or you will bounce, or, worse, cause a 
crash.

Taxiing:  Very comfortable!  All it takes to get her 
moving is a touch of throttle.  Judicious use of rudder 
and tapping of the F11 & F12 brakes handles all taxiing 
situations.

Single engine capability is good, though it could get 
exceedingly hairy if it occurs on takeoff.  The torque on 
one of the big P&W 2800's could roll you over in an 
instant if not caught immediately.

I set the SIM realism at 5 for this aircraft and, under 
the OPTIONS\JOYSTICK menu,  I set all the joystick 
sensitivities at 4 1/2.

Takeoff and Landing the B-26:

   Takeoff -  Fly it off at 110K (125mph)
              Single engine airspeed 118K (135mph)
   Downwind - 1,000 feet above runway, 150K, drop 1 notch  
              flaps. (Slow it down early!)
   Base leg - Drop down to 800 ft above R/W, hold 135 to  
              140K.
   Final    - Try to hold 125K, drop flaps to 3/4.  Gear
              down.  Flat approach on VASI, no more than  
              500fpm rate of descent.  Over Fence -  
              holding some power on, slowly bleed off       
              airspeed and rate of descent, raise nose      
              just slightly.  Throttle to idle if over
              shooting.  Fly it right to the ground  
              and at touchdown, give it some forward stick  
              to plant the nosewheel. Brake as needed.

Stalls:  Clean, power off - 110K IAS
         G & FF, power off -  90K IAS

Max Diving Speed:  370K (425mph)

Average eventual airspeed at full throttle, straight and 
level, will put you at approximately 290K IAS (333mph).  
She dives nicely (redline at 370K!) and will do reasonable 
acrobatic maneuvers.

The "book" calls for maximum manifold pressure of 52" but 
I have no idea how to obtain such readings in FSFS.  Once 
at high speed, this B-26 is a devil to slow down.  I 
usually cheat and drop flaps occasionally to kill off 
excessive airspeed.  
             ************************

Distribution Information:
=========================
This model may not be sold as part of any shareware or freeware
collection.  It may be distributed freely on Bulletin Boards and
on-line electronic services, as long as no charge is made for this
file other than normal connect charges or subscription charges to 
the service.

*******
Flight Simulator is a registered trademark of Bruce Artwick.
Flight Simulator Flight Shop is a trademark of BAO Publishing.


Bill Cline [74547,103]    Russell Mueller [76662,1623]