Rosenthal Engineering P.O.Box 1650, San Luis Obispo CA USA 93406         
              Copyright (C) 1993, 1994, 1996 All rights reserved.


                          Disk Drive Cleaner


When  used with the special, NON-ABRASIVE, cleaning diskette  and  solvent 
available  from Rosenthal Engineering, this program safely removes  debris 
from  the  delicate  read/write heads of floppy disk  drives.  Data  loss, 
unreliable  performance  and  errors can often be  traced  to  microscopic 
foreign  particles;  dirt, dust, oxides and smoke that accumulate  on  the 
disk drive heads.

         -    -    -    -    -    -    -    -    -    -    -    -

How to Use Disk Drive Cleaner 

Copy  the  program and documentation to a working directory on  your  hard 
drive. If your floppy drive ever becomes so contaminated that it will  not  
read  a  floppy  diskette, you will not be able to  read  the  Disk  Drive 
Cleaner program from a floppy disk either. Save it on your hard drive now!

To  safely and effectively clean a floppy disk drive, dispense five  drops 
of  the cleaning solution, supplied with the kit, onto the fabric  exposed 
by  the  head access slot of the special cleaning diskette.  The  cleaning 
solution  is  isopropyl alcohol, so use appropriate precautions  to  avoid 
heat, flames and eye contact. 

Insert  the cleaner diskette into the drive normally. Different  areas  of 
the  cleaning  disk  are reserved for scrubbing,  cleaning  and  polishing 
operations to avoid recontaminating the progressively cleaned heads.  Only 
Rosenthal  Engineering approved, NON-ABRASIVE cleaning disks may  be  used 
with this program. The fabric material of these diskettes is less abrasive 
than the industry specifications for the actual magnetic recording media.

Run  the Disk Drive Cleaner program from the DOS prompt. The program  will 
prompt  you to enter the letter of the drive to clean. The  whole  process 
takes less than four minutes to clean even the dirtiest drives.

Take out the cleaning diskette. That's it, you're done!

         -    -    -    -    -    -    -    -    -    -    -    -

How to Obtain Approved cleaning kits.

The  file  ORDER.FRM  contains a convenient order  form  to  register  the 
software  and order additional cleaning kits. Only  NON-ABRASIVE  cleaning 
kits, approved by Rosenthal Engineering may be used with this program. 

Orders Outside the U.S.

All  international  orders  are sent by air-mail.  See  the  order  form 
(ORDER.FRM) for shipping and handling rates.

Yes! Visa or Master Card can now be accepted and makes currency exchange 
to US Dollars very simple.

Please be sure to make your payment in "US Dollars" either by (US) cash, 
Visa  or Master Card, international money order or check drawn on  a  US 
member bank. Otherwise banks want a fifty dollar processing fee to  cash 
a twenty five dollar check. Sorry, euro-checks can not be processed.

         -    -    -    -    -    -    -    -    -    -    -    -

How to Try This Software Without a Cleaning Kit

The best way to determine if any program will satisfy your needs is to try 
it  for  yourself. The Disk Drive Cleaner program may be run  without  any 
floppy diskettes in the drive for demonstration and evaluation. A  message 
warning that you have not inserted an approved, NON-ABRASIVE cleaning disk 
will  be  displayed; however the program will function normally  for  your 
evaluation. 

To be effective, the special cleaning disk presents a running torque of at 
least  0.9  ozf-in (65 gcm) with the heads loaded, so without  a  disk  in 
place,  the demonstration will be considerably quieter than  normal.  Even 
without  a  cleaning  diskette in place, you  should  have  no  difficulty 
hearing  the drive go through its distinctly different cleaning cycles  if 
you listen carefully.  

    -    -    -    -    -    -    -    -    -    -    -    -

Other Methods of Disk Drive Cleaning

There are two other methods used for cleaning floppy diskette drives.  The 
first  involves at least partial disassembly of the disk drive and  direct 
cleaning  of  the heads and should be reserved for  technically  competent 
service  personnel.  The second follows the directions printed  on  nearly 
every  cleaning disk kit available, but is not as effective as  using  the 
Disk Drive Cleaner program.

Obsolete Cleaning Method I

This  method involves directly cleaning the internal disk drive heads  and 
mechanism  and should therefor, be left to competent technical  personnel, 
regularly involved with manufacturers factory service. With the relatively 
low  cost  of new disk drives, it is rarely practical to  invest  in  this 
level of service, unless the drive is special or particularly expensive to 
replace;  For  example, drives used in automatic  mass  disk  duplicators. 
Standard  drives  may  be  easily replaced, and  new  drives  are  usually 
available  for  about the same (and often less) cost of repairing  a  worn 
drive.

If a drive is particularly filled with debris, say from attempting to read 
a  diskette  buttered with peanut-butter and jelly, this may be  the  only 
method  of salvation. The contaminated parts are gently cleaned with  soft 
cotton  rags  and isopropyl alcohol. Several rags are used  so  the  parts 
become  progressively cleaned with fresh clean rags. Care is made  to  not 
recontaminate a freshly cleaned surface with a dirty cleaning implement.

Cleaning  the heads themselves must be done extremely  delicately.  Inside 
the  outer  plastic  (Poly  Chloride) jacket  of  a  floppy  diskette,  is 
substrate  material (polyethylene terephthalate), thinly (.0001 inch or  2 
um  nominal)  coated  with  iron oxide (rust) and  a  binder.   The  heads 
themselves are designed to make intimate contact and ride directly on  the 
magnetic  medium.  A delicate spring forces the read/write heads  to  ride 
against this very thin magnetic surface. Technicians must use extreme care 
not  to  exceed  the  the pressure normally exerted  by  the  spring  when 
burnishing the heads.

To be effective, burnishing heads must be done in-line with the read/write 
head gap. A read/write head is a very small core wound with a coil of fine 
wire. You can picture these tiny heads as a donut or bead (toroid) with  a 
fine  slot  cut through it from the center to the outside. The  toroid  is 
then embedded in a ceramic or plastic material so the slot, or head gap as 
it's  called,  is exposed at a polished surface to  contact  the  magnetic 
medium. The head gap rides perpendicular to the direction of travel of the 
disk  lined up like the spokes of a wheel, and should be cleaned  in  that 
direction.  When burnishing, the heads and cleaning fabric must be  passed 
back and forth across the head gap following a radial path like the spokes 
and the diskette being the wheel. Technicians cleaning the heads  directly 
can  use   isopropyl alcohol and "Lintless Head Cleaning  Swabs"  (General 
Cement  #GC 32-3081 or Radio Shack #44-1094). Again, use several swabs  so 
the  head is not recontaminated, as the surface area of the swabs  is  far 
less than that of a cleaning diskette. This burnishing should be  followed 
up  with a normal cleaning using the Disk Drive Cleaning program, as  your 
human  technician  (I hope this applies), can not physically  burnish  the 
heads at the same high speeds the program does so effectively.

Technicians will also notice that the program will exercise the drive  and 
heads with or without the cleaning disk in place. This can often be useful 
when  freeing  a  drive mechanism  or  lubricating  (*SPARINGLY  PLEASE!*) 
sliding and bearing parts.   

Obsolete Cleaning Method II

This  is  the "smear it around" method described on the package  of  every 
cleaning  disk kit I've seen. You apply their cleaning solution  to  their 
paper or fabric cleaning diskette. The user then enters a DOS command like 
DIR and the computer tries unsuccessfully to read the single outside track 
until  it  gives up with an error. Abrasion is not generally  of  concern, 
because the heads are not oscillated or burnished across the cleaning disk 
and the disk only runs for about thirty seconds or less.     

In  this "smear it around" method, only a very small area of the  cleaning 
disk  is used, and no effort is made to reserve different portions of  the 
cleaning  diskette  for progressively cleaner operations.  The  relatively 
small  area  of  the cleaning diskette that is  accessed  quickly  becomes 
contaminated, and the absolute maximum usage that can be squeezed out of a 
cleaning  disk  is between ten and fifteen times. Dirt from the  heads  is 
shared with the cleaning disk, and visa versa, until all are about equal.

With no effort made to burnish the heads against the cleaning surface in a 
lateral gyrating radial motion (like cleaning spokes on a wheel) the  most 
critical  head gap area is not serviced as effectively as the  Disk  Drive 
Cleaner program does. The remaining residue is left to attract more debris 
so  most of these "smear it around" method kits recommend repeat  cleaning 
after only forty hours of use, or less.

If a disk drive becomes so contaminated that it won't read the Disk  Drive 
Cleaner  reliably, you will get a DOS error message or an "Error!  Program 
is  corrupt." message. The only advantage to the "smear it around"  method 
is to hopefully get the disk drive clean enough to at least load the  Disk 
Drive Cleaner program. It's best to keep a copy of the Disk Drive  Cleaner 
on  your hard drive so you won't be depending on the same drive  that  has 
become unreliable to load the program.

Other Drive Cleaning Considerations

Modern  computers  employ cooling fans to circulate air through  them  for 
efficient  operation.  Unfortunately, along with the air  comes  dust  and 
other particles. Sometimes the dust will accumulate sufficiently to  cause 
mechanical problems with floppy disk drives. For example, there is a small 
hole near the center of the diskette which the computer uses to index  and 
determine the position of the rotating disk. An electric eye, made up of a 
photo  cell and a (often invisible infared) light emitting  diode  watches 
the  hole. Other electric eyes monitor other holes and notches  for  write 
protection, media type, disk in position, etc. If dust accumulates to  the 
point  that any of these electric eye sensors become obscured, they  won't 
function  properly.  This  is rarely a problem, and can  be  corrected  by 
simply  vacuuming the disk drive through the slot. There are  small,  cute 
vacuum cleaners sold for this, but just use a standard tank and hose  type 
vacuum  cleaner  with a small crevice tool attached. There is no  need  to 
invade  the disk drive itself. If more cleaning is required, it should  be 
done  by a competent service technician. This type of cleaning  is  rarely 
required, but its description is included to be complete. 

    -    -    -    -    -    -    -    -    -    -    -    -

Failures Caused by Dirty Disk Drive Heads

The floppy disk drive read/write heads actually contact the magnetic oxide 
coating of the floppy diskette itself. This magnetic coating is very thin, 
in  fact  the  thinner,  the  better, about  0.0001  inches  or  less.  To 
understand  how thin this is, a human hair is 0.003" (30 times larger),  a 
dust  particle is .0015" (15 times larger), a finger print is 0.006"  (six 
times  larger) and a tobacco smoke particle 0.00025 (2 1/2 times  larger). 
The  smallest  separation of the head from the oxide  coating  will  cause 
errors transferring data between the head and the diskette.

Additionally diskettes are finished to a surface roughness of 3  microinch 
(76 um)AA maximum.... That means shiny smooth. The diskette rubs  directly 
against  the head at about 300-360 RPM, so this is no place for  dirt  and 
grit  abrasive to the surface. With clean heads, a good  quality  diskette 
will  typically  have life expectancy for media wear of 5  million  passes 
minimum.  

Clean,  well  maintained  disk  drives  are  more  reliable  and   prevent 
accelerated wear and diskette deterioration.

    -    -    -    -    -    -    -    -    -    -    -    -

How Diskette Quality Affects Disk Heads

As  the  coating of magnetic oxide passes across the head gap,  a  writing 
current  passed through its windings forms an electromagnet that causes  a 
magnetic flux to take the most conductive path across the gap in the head. 
Providing  this  gap is clean (especially of magnetic  oxides),  the  most 
magnetically  conductive path is the surface of the oxide  coating,  which 
becomes magnetized and remains so even after the disk is removed. The data 
is stored as high as 17,436 bits (1's and 0's) per inch on a surface  less 
than one sixth the thickness of a finger print. 

Reading  the information back off the diskette is even more  critical.  As 
the  magnetic medium passes across the head gap, the very tiny  magnetized 
particles induce a voltage in the read/write head which recovers the data. 
As  the dirt builds up between the magnetic medium and the  critical  head 
gap, the effective clipping rate deteriorates.
 
The industry standard (ANSI) sets the minimum magnetic clipping level  for 
diskettes  at  40%. Typically a better quality diskette will be  rated  at 
least  60% and some even as good as 70%. A good judge of the quality of  a 
diskette is the guaranteed minimum clipping level, but you'll have to  ask 
the manufacturer. 

A  dropout  (which is a loss of data) is defined as signal level  with  an 
insufficient amplitude to be read consistently by the system. For example, 
a signal written at 6.0 volts and read back at 2.4 volts represents a  60% 
loss  in  signal amplitude, which means a signal of 40% remaining  (a  40% 
clipping  level).  When dirt accumulates at the head  gap,  the  recovered 
signal  deteriorates  rapidly  and when a clipping rate  falls  below  the 
industry standard, it is considered a missing bit (drop out) error.

Another  error  that  increases  as  the  disk  read/write  heads   become 
contaminated  affects  the  peak voltage variance,  or  modulation  error. 
Modulation  is the difference (or variation) from the average signal.  For 
example,  if an average signal level produced when a diskette  passes  the 
head  gap is 6.0 volts, but within a five millisecond time span  rises  to 
6.6 volts, a modulation error of 10% has been measured. This error  causes 
inaccurate write/read responses and becomes especially pronounced when the 
diskette is of low quality, damaged, irregular or the heads were not clean 
when the disk was recorded.

With  the  close  tolerances required to  write  and  recover  information 
between  the  heads  and the diskette, the  importance  of  using  quality 
diskettes and periodically cleaning disk drives is obvious.

    -    -    -    -    -    -    -    -    -    -    -    -

How to Handle and Store Diskettes

1) No smoking. 

Tobacco  smoke  is  one  of the worst substances  for  causing  damage  to 
diskettes.  Smoke particles are about two to three times the thickness  of 
the diskettes magnetic oxide coating and are particularly nasty because of 
their  sticky  tar  nature. Airborne smoke particles are  drawn  into  the 
computer  and  circulated by the cooling fan. Smoke  particles  are  about 
1/7th the size of dust particles, so air filters that trap the majority of 
dust may not restrict the smoke. Diskettes exposed to the air in the  area 
around  the  computer are extremely vulnerable to  smoke  particles.  Air, 
especially  around  high voltage sources like CRT monitors,  gets  charged 
with static electricity. The electrostaticly charged smoke particles  then 
adhere  to surfaces around the computer and the smoker.  Floppy  diskettes 
have  a  particular  affinity to tobacco smoke,  especially  if  they  are 
exposed by being left out of their protective envelopes and storage boxes.

2) Keep a Clean Work Environment.

Wash  your  hands and don't eat or drink when  handling  diskettes.   When 
inserted  into  a disk drive, the contamination on the  diskette  will  be 
scraped   onto  the  read/write  heads.  The  heads  should   be   cleaned 
periodically using the Disk Drive Cleaner program and cleaning kits so the 
contamination  accumulated  on  the  heads  does  not  migrate  to   other 
diskettes.  If  you exchange diskettes with others who may not  take  such 
precautions seriously, you should take it upon yourself to clean your  own 
systems drives following the exchange.  

Never  touch  or attempt to clean the surface of  the  diskettes  magnetic 
medium. 

3) Keep Diskettes Away From Magnetic Fields.

Contact   with  permanent  magnets  (like  cute   refrigerator   magnets), 
transformers  (like calculator type power supplies), electric  motors  and 
telephone bells create strong magnetic fields and will destroy your  data. 
Keep  magnetic  fields away from diskettes and never allow magnets  to  be 
around your computer work area.

4) Don't Physically Abuse a Diskette.

Don't  bend,  fold,  paper clip, rubber band or  place  heavy  objects  on 
diskettes.  Use  only felt tip pens to gently write  on  diskette  labels, 
never  ball point pens and pencils. Keep diskettes out of direct  sunlight 
and heat. Any of these will cause damage and loss of data.

    -    -    -    -    -    -    -    -    -    -    -    -

                  Protecting Your Valuable Data

The  best time to deal with a computer related problem is before you  have 
one.

Backup Copies

The  best way to protect your valuable data is to make copies of  it,  and 
keep it in a safe place, preferably at a different location. Safety backup 
disks  made on computers properly maintained with the Disk Drive  Cleaner, 
are more reliable should they ever be required.

Periodic Maintenance

Regularly scheduled periodic cleaning of your computers floppy disk drives 
will  reduce  data  loss,  unreliable performance  and  errors  caused  by 
microscopic   foreign  particles,  dirt,  dust,  oxides  and  smoke   that 
accumulates on the disk drive heads.

How  often  you  need  to  use the Disk  Drive  Cleaner  depends  on  your 
computer's  environment, the amount of use your floppy disk drive  receive 
and the quality and cleanliness of the diskettes you use.

For  automatically fed disk drives employed in mass disk duplication on  a 
continuous  full  time  basis, it's not uncommon to  use  the  Disk  Drive 
Cleaner  daily. These drives are usually specially modified for this  type 
of service and are often quite expensive. If distribution disks are to  be 
of  consistently good quality, the drives must be properly maintained  and 
clean.  Well  cleaned drives will produce better results and  last  longer 
with less repairs and down time.

For  computers  in most non-smoking offices,  most  diskette  manufactures 
recommend  cleaning diskette drives after only 40 hours of use,  and  more 
often in environments of dust, smoke and dirt. Once every six months seems 
to satisfy the requirements of the majority of computer users.

Cleaning  disks used in non-smoking, low dirt and dust offices seem to  be 
effective  for  at least ten to fifteen uses with this  program.  Use  the 
ORDER.FRM  file for ordering additional cleaning kits. Always order a  few 
extra  kits in the sizes you use, so you won't run out when you need  them 
the most. 

         -    -    -    -    -    -    -    -    -    -    -    -

                           Program Requirements

Disk  Drive Cleaner runs using DOS 3.0 or higher and has been tested  with 
versions  through  7.  This program supports the  approved  cleaning  kits 
available  for  all  3 1/2" and 5 1/4" double  sided  floppy  disk  drives 
configured as drives A-C. Sorry but 8" and single sided approved  cleaning 
kits  are not available except by special request. Use  only  NON-ABRASIVE 
cleaning  disks  approved  by  Rosenthal Engineering  for  use  with  this 
program.  This program will run under Windows but because it  dose  direct 
hardware  control, you'll get better performance if you shut down  Windows 
and restart under DOS.

         -    -    -    -    -    -    -    -    -    -    -    -

                   CD-Rom, Magazine and Book Publishers

Publishers  are encouraged to include "Rosenthal Virus Simulator (tm)"  as 
shareware  with  CD-Rom collections, books and magazines.  Please  contact 
Rosenthal Engineering directly.

         -    -    -    -    -    -    -    -    -    -    -    -

                        Software License agreement


You  are  encouraged  to copy and distribute  this  software  provided  it 
remains unmodified, complete in its original form, and no fee (other  than 
a  nominal  copy charge) is required. This software is  provided  "as  is" 
without warranty either expressed or implied.

You may not make any changes or modifications to the software, and you may 
not decompile, disassemble or in anyway reverse engineer the software. 

This  software  is  provided  "as is"  without  warranties  of  any  kind. 
Responsibility rests entirely with the user to determine its fitness for a 
particular purpose. ROSENTHAL ENGINEERING SHALL NOT IN ANY CASE BE  LIABLE 
FOR SPECIAL, INCIDENTAL, CONSEQUENTIAL, INDIRECT OR OTHER SIMILAR  DAMAGES 
ARISING  FROM  ANY USE OF THIS SOFTWARE. Some states may not  allow  these 
limits  on  warranties,  so they may not apply to you. In  no  case  shall 
Rosenthal  Engineering's liability exceed the license fees paid by you  to 
Rosenthal  Engineering  for the right to use the Licensed  Software.  Use, 
duplication, or disclosure by the U.S. Government of the computer software 
and  documentation  in  this package shall be subject  to  the  restricted 
rights  applicable  to  commercial  computer  software  as  set  forth  in 
subdivision  (b)  (3) (ii) of the Rights in Technical  Data  and  Computer 
Software    clause    at    252.227-7013    (DFARS    52.227-7013).    The 
Contractor/manufacturer is Doren Rosenthal, Rosenthal Engineering, P.O.Box 
1650, San Luis Obispo, California 93406.

This  constitutes  the  entire agreement  and  understanding  between  the 
parties  and supersedes any prior agreement or understanding whether  oral 
or written and may only be modified in writing.


         -    -    -    -    -    -    -    -    -    -    -    -

                        Cleaning Solution


The  disk  drive cleaning kit comes complete with isopropyl alcohol  in  a 
small  bottle  that makes it convenient to dispense for cleaning.  If  you 
require additional solvent, isopropyl alcohol is the same ingredient found 
in  common rubbing alcohol and is available quite inexpensively  from  any 
pharmacy. 

Warning!  Isopropyl alcohol is flammable. Keep away from heat and  flames. 
Keep  the  cap  tightly secured when not in use and out of  the  reach  of 
children.  Isopropyl alcohol is irritating to eyes, so avoid eye  contact. 
If eye contact occurs, immediately flush eyes with plenty of water for  at 
least ten minutes and call a physician.

================================================================  

Material Safety Data Sheet                        June 16, 1993

Rosenthal Engineering
P.O.Box 1650
San Luis Obispo, CA USA 93406

Trade name:    Disk Drive Head Cleaning Kit ( Fluid )

----------------------------------------------------------------
1)   Ingredient
          Isopropyl Alcohol
          C.A.S. Number ..............  67-63-0
          Percent.....................  100%
----------------------------------------------------------------
2)   Physical Data
          Boiling point...............  ca.  180.0 F
          Vapor Pressure..............  ca   33.0 mmHg
          Vapor Density...............  ca.  5.0  Air=1
          Evaporation rate............  ca.  0.80 Water=1
          Solubility in water.........  ca.  100.0 g/100 cc
          Specific gravity............  ca   0.800 Water=1
          Percent volatile............  100
          Volatile organic compounds..  785.00 gms/liter
          VOC less H2O & exempt solvents     N/D
          ph..........................  4.7
          Viscosity...................  N/D
          Melting point...............  N/D

          Appearance..................  Clear liquid
          Odor........................  Alcohol odor
----------------------------------------------------------------
3)   Fire and Explosion Hazard Data
          Flash Point.................  ca.  53.0 F
          Flammable limits - LEL......  ca.  2.0%
          Flammable limits - UEL......  ca.  12.0%
          Autoignition temperature....  N/D
     
          Extinguishing media.........  CO2, Foam, Dry  Chemical, 
                                        Water Fog
 
          Special fire fighting procedures......  None
          Unsual fire and explosion hazards.....  None
          NFPA Hazard codes
               Health...........................  2
               Fire.............................  3
               Reactivity.......................  0
               Unusual reaction hazard..........  None
----------------------------------------------------------------
4)   Reactivity Data

          Stability.............................  Stable

          Incompatibility:
               Materials/Conditions to avoid....  Heat

          Hazardous Polymerization:
               Hazardous polymerization will not occur.

          Hazardous decomposition products:
               Carbon Monoxide and Carbon Dioxide.
----------------------------------------------------------------
5)   Environmental information

Spill Response:
     Refer  to  other  sections  of  this  MSDS  for  information 
     regarding   physical   and   health   hazards,   respiratory 
     protection,  ventilation and personal protective  equipment. 
     Extinguish  all ignition sources. Cover and collect  spilled 
     fluid  with absorbent material such as a paper wiping  towel 
     and clean up residue. Place in an approved metal container.

          Recommended Disposal:
               Incinerate   in   an  industrial   or   commercial 
               facility.

          Environmental data:
               Material  to be disposed has a U.S. EPA  hazardous 
               number D001 (ignitable).

               SARA Hazard Class.........    Yes
               Pressure..................    No
               Reactivity................    No
               Acute.....................    Yes
               Chronic...................    Yes
----------------------------------------------------------------
6)   Suggested First Aid
          Eye Contact:
               Immediately  flush  eyes  with  large  amounts  of 
               water. Get immediate medical attention.

          Skin Contact:
               Flush  skin  with  large  amounts  of  water.   If 
               irritation persists, get medical attention.

          Inhalation:
               If  signs/symptoms occur, remove person  to  fresh 
               air. If signs/symptoms continue, call physician.

          If Swallowed:
               If  swallowed, call a physician immediately.  Only 
               induce  vomiting at the instruction of a physician.
               Never  give anything by mouth to an unconscious 
               person.
----------------------------------------------------------------
7)   Precautionary information.
          Eye protection................     Avoid eye contact.
          Skin protection...............     Avoid skin contact.
          Recommended ventilation.. Use in a well ventilated area.
          Respiratory protection... Avoid inhalation of vapors.
          Prevention of Accidental Ingestion... Do not ingest.
          Recommended storage... Keep out of the reach of children.

          Fire  and Explosion Avoidance:
               Keep away from heat, sparks, open flame, and other 
               sources of ignition.

     Exposure Limits

Ingredient               Value     Unit   Type    Auth   Skin*
---------------------    -----     ----   ----    ----   -----
Isopropyl Alcohol....    400       PPM    TWA     ACGIH
Isopropyl Alcohol....    985       MG/M3  TWA     ACGIH
Isopropyl Alcohol....    500       PPM    STEL    ACGIH
Isopropyl Alcohol....   1230       MG/M3  STEL    ACGIH 
Isopropyl Alcohol....    400       PPM    TWA     OSHA    
Isopropyl Alcohol....    980       MG/M3  TWA     OSHA
Isopropyl Alcohol....    500       PPM    STEL    OSHA
Isopropyl Alcohol....   1225       MG/M3  STEL    OSHA 

*  Skin Notation: Listed substances indicate with "Y" under  SKIN 
refer  to the potential contribution to the overall  exposure  by 
the cutaneous route including mucous membrane and eye, either  by 
airborne  or,  more  particularly, by  direct  contact  with  the 
substance. Vehicles can alter skin absorption.

Source of Exposure Limit Data:

ACGIH: American Conference of Governmental Industrial Hygienists.
OSHA:  Occupation Safety and Health Administration.
----------------------------------------------------------------
8)   Health Hazard Data

Eye Contact:
     Moderate  Eye  Irritation: signs/symptoms  include  redness, 
     swelling, pain, tearing, and hazy vision.

Skin Contact:
     Mild Skin Irritation (after prolonged or repeated contact):
     signs/symptoms can include redness, swelling, and itching.

PERSONS WITH PRE-EXISTING SKIN DISORDERS MAY BE MORE  SUSCEPTIBLE 
TO DERMATITIS.

Inhalation:
     Central   Nervous  System  Depression:  signs/symptoms   can      
     include  headache,  dizziness,  drowsiness,  incoordination,      
     slowed   reaction  time,  slurred  speech,   giddiness   and      
     unconsciousness.

     Irritation    (upper   respiratory):   signs/symptoms    can           
     include  soreness  of  the nose  and  throat,  coughing  and 
     sneezing.

If Swallowed:
     Ingestion may cause: Irritation of Gastrointestinal Tissues: 
     signs/symptoms   can  include  pain,   vomiting,   abdominal 
     tenderness, nausea, blood in vomitus, and blood in feces.
    
     Central   Nervious System  Depression:  signs/symptoms   can 
     include headache, dizziness, drowsiness, muscular  weakness, 
     incoordination,  slowed  reaction  time,  fatigue,   blurred 
     vision, slurred speech, giddiness, tremors and convulsions.

     Aspiration Pneumonitus: signs/symptoms can include coughing, 
     difficulty  breathing, wheezing, coughing up and  pneumonia, 
     which can be fatal.

Other Health Hazard Information:

DUE TO THE SIZE OF THE CONTAINERS AND THE POTENTIAL LOW LEVEL  OF 
EXPOSURE  TO THIS PRODUCT, MANY OF THESE HEALTH EFFECTS  ARE  NOT 
EXPECTED TO OCCUR UNDER ANTICIPATED USE CONDITIONS.

--------------------------------------------------------------
Abbreviations: N/D - Not Determined     N/A - Not Applicable
--------------------------------------------------------------

The  information on this Data Sheet represents our  current  data 
and  best  opinion  as to the proper use  and  handling  of  this 
product under normal conditions. Any use of the product which  is 
not  in conformance with this Data Sheet or which involves  using 
the  product in combination with any other product or  any  other 
process is the responsibility of the user.
===============================================================