*****************************  SYSTEM  *************************************

ASM32 system subroutines Copyright (C) 1993 - 1995 Douglas Herr
all rights reserved


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

COLOR16:     calculate color value for palette register
Source:      color16.asm

Call with:   EBX pointing to red value (0-3), green value (0-3)
             and blue value (0-3); see also Palette16
Returns:     AH = color value for 16-color palette register
Uses:        AH
Supports:    VGA 16-color modes (text or graphics)
             EGA 16-color modes, except with CGA monitor
Example:

extrn   color16:near

include dataseg.inc

c16     db 3                  ; brightest red
        db 1                  ; dim green
        db 0                  ; no blue

@curseg ends

include codeseg.inc
        .
        .
        .
        lea   ebx,c16
        call  color16




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EXENAME:     determine the full path and filename of the executing program
Source:      exename.asm (strlen.asm)

Call with:   no parameters
Returns:     ECX = length of program name string
(CauseWay FLAT model)
             [EBX] = near pointer to the name of the executing program,
             including drive and full path.

(all except CauseWay FLAT model)
             ES:[EBX] = far pointer to the the name of the executing program,
             including drive and full path.

             The filename returned is an ASCIIZ string in the program's
             environment segment.

(all except CauseWay FLAT model)
             Version 2.0: Note that EXENAME does not copy the program name to
             near data.  It returns a far pointer to the program name which
             you may copy to near data with STRNDUP if you wish.

Uses:        ES (except CW FLAT model), EBX, ECX, flags
Example:

extrn   exename:near

include codeseg.inc

        .
        .
        .
        call    exename         ; string returned at ES:[EBX]
IFNDEF  FLATMODEL
        call    strndup         ; copy to near data area
ENDIF
      




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EXESIZE:     determine size of .EXE program
Source:      exesize.asm

Call with:   [EDX] pointing to ASCIIZ .EXE filename
Returns:     if CF = 1, AX = DOS error code
                        if AX = 0, not an EXE-format file
             if CF = 0, EAX = bytes in .EXE file loaded by DOS program
                        loader and by CauseWay
             Note that additional data may be copied to the end of a DOS
             .EXE file with the DOS COPY /B command.  This is handy for
             help screens or other such data that you want to keep with
             the .EXE file, but that you don't want to be loaded in memory
             with the program.  If you do copy additional data to the .EXE
             file, EXESize will report only the portion of the file loaded
             in RAM by the DOS program loader and CauseWay, while FSize (in
             DISK.DOC) reports the entire file size.
Uses:        EAX, flags
Example:

;
; code used to test EXEsize
;
include model.inc

public  testcode
extrn   exename:near, exesize:near
extrn   strndup:near, i4tostr:near
extrn   tprint:near, getkey:near

include dataseg.inc
extrn   pspseg:word
space   db 20 dup(0)
@curseg ends

include codeseg.inc
testcode        proc near
        mov     es,pspseg
        call    exename         ; get name of this program
        call    strndup         ; copy to near heap
                                ; startup code was assembled with /DHEAP
        mov     edx,ebx         ; [EDX] -> EXE filename
        call    exesize         ; EAX = EXE program size
        lea     esi,space
        call    i4tostr         ; convert to ASCIIZ string
        xor     edx,edx         ; point to UL corner of screen
        mov     ah,12           ; "can't miss it" color
        call    tprint          ; print it
        call    getkey          ; don't scroll off screen yet
        ret                     ; go back to calling code
testcode        endp

@curseg ends
        end



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOPPIES:    determine the number of floppy disk drives intalled
Source:      floppies.asm

Call with:   no parameters
Returns:     AX = number of floppy drives
Uses:        AX; all other registers and flags are saved
Example:

include model.inc

extrn   floppies:near

include codeseg.inc

myproc  proc   near
        .
        call   floppies



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOPPYTYPE:  determine the type of floppy disk drives intalled
Source:      floptype.asm

Call with:   DL = drive number (0 = drive A:)
Returns:     AX = floppy drive type
              0 = invalid drive number
              1 = 360k
              2 = 1.2M
              3 = 720k
              4 = 1.44M
Uses:        AX, flags
Example:

include model.inc

public  myproc
extrn   floppytype:near

.data
drive_number   db 0

.code
myproc  proc
        .
        mov    dl,drive_number
        call   floppytype
        or     ax,ax
        jz     bad_drive_number


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETCPU:      detects cpu type
Source:      getcpu.asm

Call with:   no parameters
Returns:     AX = 3 if 386 (SX or DX)
             AX = 4 if 486 (SX or DX)
Uses:        AX
Example:     call   getcpu



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETCRT:      determines active monitor type
Source:      getcrt.asm ($herc.asm, isevga.asm)

Call with:   no parameters
Returns:     AX = code for active video system
             CGA = -1
             MDA = 0
             EGA mono = 0100h
             VGA mono = 0300h
             EGA color = 1
             MCGA = 2
             VGA color = 3
             HGC = 128
             HGC+ = 144
             InColor = 208
             Note: GetCRT may be re-assembled with the /DNOHERC switch
             to eliminate code which detects Hercules equipment
Uses:        AX
Supports:    CGA, MCGA, MDA, HGC, HGC+, InColor, EGA, VGA
Example:     call    getcrt




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

INSERT:      control INSERT key status
Source:      insert.asm (cw$info.asm)

Call with:   AL = 0 to turn INSERT off in BIOS data area
             AL = 1 to turn INSERT on in BIOS data area
Returns:     nothing
Uses:        nothing
Example:

include codeseg.inc

extrn   insert:near

; code

        mov     al,1         ; turn INSERT on in BIOS data area
        call    insert



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISANSI:      determines if ANSI or compatible is loaded and active
Source:      isansi.asm

Call with:   no parameters
Returns:     CF = 1 if no ANSI device driver loaded and active
             CF = 0 if ANSI loaded and active
Uses:        CF
Example:

include codeseg.inc

extrn   isansi:near

; code
        .
        .
        .
        call   isansi         ; let's see if ansi.sys is loaded
        jc     no_ansi        ; jump if not




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISATT:       determines if an ATT 6300-type display card is installed
             This equipment is like a CGA except that it has an additional
             640 x 400 2-color graphics mode (mode 40h)
Source:      isatt.asm ($6845.asm, isevga.asm)

Call with:   no parameters
Returns:     if CF = 1, ATT 6300 display not present
             if CF = 0, ATT 6300 display is installed
Uses:        flags
Example:

public  cgamode

extrn   isatt:near

include codeseg.inc

cgamode proc    near
        mov     ax,06h             ; default: set CGA mode
        call    isatt              ; see if mode 40h is available
        jc      short set_mode     ;  nope
        mov     ax,40h             ; use ATT 6300 mode 40h
set_mode:
        int     10h                ; use BIOS to set mode
        ret

cgamode endp

@curseg ends
        end



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISEVGA:      determines if an EGA or VGA is installed
Source:      isevga.asm

Call with:   no parameters
Returns:     if CF = 1, no EGA or VGA
             if CF = 0
               DX = video memory in kbytes
               AL = monitor type
                AL = -1 if monitor is CGA
                AL = 0 if monitor is monochrome
                AL = 1 if monitor is EGA or better

               AH = EGA/VGA flag
                AH = 1 if EGA
                AH = 3 if VGA

Uses:        AX, DX, CF
Example:

include codeseg.inc

extrn   isevga:near

; code
        .
        .
        .
        call   isevga
        jc     no_evga




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISHERC:      determines if a Hercules card or compatible is installed
             and if so, determines if it is the active video system.
Source:      isherc.asm ($herc.asm)

Call with:   no parameters
Returns:     if CF = 1, no Hercules or compatible installed
             if CF = 0, AX = Hercules model
             128 = Hercules Graphics Card or compatible; active
             144 = Hercules Graphics Card Plus; active
             208 = Hercules InColor card; active
             -128 = Hercules Graphics Card or compatible; not active
             -144 = Hercules Graphics Card Plus; not active
             -208 = Hercules InColor card; not active
Uses:        AX, CF; all other flags and registers are saved
Example:

include codeseg.inc

extrn   isherc:near

; code
        .
        .
        .
        call  isherc
        jc    no_herc


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISMONO:      detects a monochrome-compatible video card
             this is handy in 2-monitor systems.
Source:      $6845.asm

Call with:   no parameters
Returns:     if CF = 1, no monochrome monitor
             if CF = 0, monochrome monitor is installed
                        including Hercules InColor
Uses:        flags
Supports:    MDA, EGA & VGA MONO, HGC, HGC+, InColor
Example:

include codeseg.inc

extrn   ismono:near

; code
        .
        .
        .
        call  ismono
        jc    no_monochrome




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISMOUSE:     determines if a mouse is installed
Source:      ismouse.asm

Call with:   no parameters
Returns:     if CF = 0, AX = number of mouse buttons
             if CF = 1, no mouse or mouse driver not installed
Uses:        AX, flags
Example:

include  codeseg.inc

extrn    ismouse:near

; code
        .
        .
        .
        call    ismouse
        jc      no_mouse




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISSEVGA:     determines if a Super EGA or Super VGA is installed
Source:      issevga.asm

Call with:   no parameters
Returns:     if CF = 1, no Super EGA or Super VGA recognized by ASM32

             if CF = 0

              if AH = 1: (Super EGA)
               AL = 1 if Paradise EGA 480
               AL = 2 if Everex EGA

              if AH = 3: (Super VGA)
               AL = 1 if Paradise VGA
               AL = 3 if Tseng VGA chipset
               AL = 4 if Oak VGA
               AL = 5 if Western Digital VGA chipset

             See also IsEVGA and WhichVGA
Uses:        AX, CF
Example:

include codeseg.inc

extrn   issevga:near

; code
        .
        .
        .
        call   issevga
        jc     no_superevga




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISVBE:       determines if VESA Video BIOS Extension (VBE) is installed
Source:      isvbe.asm

Call with:   no parameters
Returns:     if CF = 1, no VBE video card installed
             if CF = 0, EBX = near pointer to VESA info data structure

             The VESA information data structure in IsVBE is similar to
             the information structure returned by VESA function AX = 4F00h
             except that IsVBE copies the data to 32-bit memory and converts
             the OEMSTR and VIDEOMODEPTR pointers from real-mode addresses to
             32-bit linear addresses.  See VESA VBE documentation for
             description of VGAInfoBlock fields.

Uses:        EBX, CF
Supports:    VBE versions 1.x and 2.x
Known bugs:  Trident 9400CXi BIOS may return incorrect TotalMemory field.
Example:

; I want to use VESA mode 110h, a 640x480, 32k-color mode
; check for VBE, then check the VideoModePtr for 0110h

include model.inc

extrn   isvbe:near

VGAInfoBlock    struc
signature       db 'VESA'
vbever          dw ?
oemstr          dd ?
capabilities    db 4 dup(?)
VideoModePtr    dd ?
TotalMemory     dw ?
Reserved        db 236 dup(?)
pad             db 256 dup(?)
VGAInfoBlock	ends

include dataseg.inc

; external data in STARTxx.ASM
extrn   zero_sel:dword         ; selector for linear memory address
                               ; tell the assmebler it's a DWORD so it
                               ; won't add a superfluous 66h byte prefix.
@curseg ends

; (continued on next page)


; IsVBE example, continued)

include codeseg.inc
        .
        .
        .
        call    isvbe
        jc      short cant_use_0110h

;
; get linear address of list of supported modes
;
        mov     edi,[ebx].VideoModePtr
        mov     ax,0110h
        mov     es,zero_sel             ; ES:[EDI] -> list of supported modes
        cld
ck_list_end:
        cmp     word ptr es:[edi],0FFh  ; end of mode list?
        je      short cant_use_0110h
        scasw                           ; mode supported?
        jne     short ck_list_end       ;  not found yet

;
; mode 0110h is supported
; do what you want with it
;
        .
        .



;
; general failure
;
cant_use_0110h:
        .
        .
        .



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

KBDTYPE:     determines type of keyboard and functions supported
Source:      kbdtype.asm

Call with:   no parameters
Returns:     if AH = 10h, advanced keyboard functions supported
                  AL = 0 if 84-key keyboard
                  AL = 1 if 101-key keyboard

             if AH = 0, advanced keyboard functions not supported
                  AL = 0

             if advanced keyboard functions are not supported, it is
             likely the program is running on an old XT-type computer
             converted to 386 with the Intel InBoard 386/PC board.  You
             will not encounter this equipment often.

Uses:        AX, flags
Example:

; Use KBDTYPE to determine which function to use to read a keystroke

extrn   kbdtype:near

        .
        .
        .
        call    kbdtype            ; get appropriate BIOS function number
        int     16h                ; get key from keyboard buffer


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MATHCHIP:    determines if x87 math coprocessor is installed
Source:      mathchip.asm

Call with:   no parameters
Returns:     AX = code for x87 model
             0 = not installed
             2 = 287                   ; earliest 386 computers used 287
             3 = 387 (DX or SX)
             4 = 487 (DX or SX)
             If the coprocessor is present, it is initilaized by MathChip.
Uses:        AX, all x87 registers
Example:     call  mathchip





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MOUSESAVE:   save mouse state
Source:      moussave.asm

MOUSERESTORE:restore previously saved mouse state
Source:      moussave.asm

             MouseSave and MouseRestore are handy when you have installed a
             mouse event handler and you will be using the SYSTEM command,
             where some other program may reset or otherwise change the
             mouse event trapping.

             MouseSave allocates a buffer, saves the mouse state in the
             buffer, resets the mouse driver and returns the buffer address.

             MouseRestore restores a specified mouse state and releases the
             buffer.  Both MouseSave and MouseRestore assume that you already
             know there is a mouse in the system.

Call with:   MouseSave: no paramerters
             MouseRestore: AX = buffer address returned by MouseSave
Returns:     if CF = 1, AH = DOS error code
             if CF = 0, no error; MouseSave returns buffer address in AX
Uses:        AX, flags
Example:

include model.inc
extrn   msave:near, mrestore:near

include dataseg.inc
save_mouse dw 0
@curseg	ends

include codeseg.inc

        .
        .
        .

; save the mouse driver state
; I've already checked to see if there's a mouse
        call    mousesave
        jc      dos_error
        mov     save_mouse,ax
        .
        .
; some other subroutine has messed with the mouse
        mov     ax,save_mouse   ; buffer address from previous MSave
        call    mouserestore
        jc      dos_error




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

PALETTE16:   change palette in EGA, VGA or SVGA 16-color mode
             changing the palette changes the actual color associated
             with a color attribute
Source:      palet16.asm

Call with:   BH = color value (see Color16 in SYSTEM.DOC)
             BL = color attribute to map color to (0-0Fh)
             restore default palette with BX = 0FFFFh
Returns:     nothing
Uses:        nothing
Supports:    EGA, VGA, SVGA 16-color modes, text or graphics
             except EGA with CGA monitor
Example:

include codeseg.inc

extrn   color16:near, palette16:near

; data
c16     db 3                  ; brightest red
        db 1                  ; dim green
        db 0                  ; no blue

; code
        .
        .
        .
        lea   ebx,c16
        call  color16
        mov   bh,ah           ; color value in BH
        mov   bl,15           ; color attribute 0Fh
        call  palette16




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

USE32K:      limit Hercules equipment to 32k memory (128k on InColor)
USE64K:      allow full 64k on HGC and HGC+ (256k on InColor)
Source:      $herc.asm

Requires Hercules or compatible

Call with:   no parameters
             Use32k is equivalent to the Hercules "half" configuration
             Use64k is equivalent to the Hercules "full" configuration
             ASM32's default is "half".  Use this configuration if you
             have a 2-monitor system, unless you are using the Hercules
             CGA card. 
Returns:     nothing
Uses:        nothing
Example:     ; in this example I'm determining if a Hercules is installed
             ; and setting the configuration to "full"


extrn   IsHerc:near
extrn   Use64k:near

include codeseg.inc

        .
        .
        .
        call  IsHerc
        jc    no_herc
        or    ax,ax

; use_only_half if HGC is not default monitor
        js    short use_only_half
        call  use64k          ; else use all Hercules memory
use_only_half: