ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º        HWiNFO - Copyright (c)1995-96 RealSoft, All Rights Reserved.        º
 º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º
 º                  Version 3.03 ; Last Update: Oct-21-1996                 º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 *** Any comments, logfiles or questions are welcome: malik@us.svf.stuba.sk ***
 **************************************************** malik@elf.stuba.sk ******




                 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                 ³  USE THIS PROGRAM ONLY AT YOUR OWN RISK  ³
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ







  HWiNFO is a !POWERFUL! hardware detection program. The whole code is written
  in pure assembler (btw about 30,000 lines), thus it's so tiny. It is simple,
  quick and on most systems very efficient. It "tries" to give only Important
  information about all the physical things in your computer so, that you must
  not look inside the PC to see what's there. The most routines access directly
  hardware, to avoid some programs to emulate non-existing computer hardware.
  I have excluded all the unnecessary information, such as CMOS, Interrupts,
  Drivers, Partitions info and others because HWiNFO is more Hardware-oriented.
  I hope, you don't want HWiNFO to determine your mouse cable lenght or the
  speed of your computer ventilator... :-)


  The newest version is always (immediately) available at:
  SAC ftp       - ftp.elf.stuba.sk /pub/pc/utilmisc
  SAC BBS       - ++42 7 5438 232   (19,200 Baud)
                  ++42 7 5438 295   (28,800 Baud)

  At other sitez/BBS later...
  SimTel        - ftp.simtel.net /pub/simtelnet/msdos/sysinfo
  SAC mirrors   - ftp.vse.cz /pub/msdos/SAC/pub/pc/utilmisc
                  ftp.cs.tu-berlin.de /pub/msdos/mirrors/ftp.elf.stuba.sk/pub/pc/utilmisc
                  ftp-beer.bke.hu /pub/sac/pc/utilmisc
                  192.217.228.45 /SAC/pub/pc/utilmisc
  Garbo archive - garbo.uwasa.fi /pc/sysinfo




 ## Requirements ##############################################################

    - DOS 3.0 or newer
    - cca. 280 KBytes of free system memory
    - Needs to be executed from directory in which it's installed in !
      (I suggest, you don't rename the executable file)

    Well, that's all. I hope, it will work on all machines.




 ## Registration ##############################################################

  HWiNFO is shareware, meaning that you can test the program free and check
  if it is useful for you. The public version is Unregistered, but works at
  FULL Power! It's of no use to make such a Shareware version of hardware
  detection program with limited abilities. The only disadvantage is the
  message, that HWiNFO isn't registered and to press a random key while the
  results are showen.

  If you think you could use this program and don't want to see that stupid
  message, or if you continue using it after a trial period of 30 days, you
  should register. Otherwise after this period HWiNFO becomes an illegal copy
  and you have to delete it.

  If you decide to register, you should print out the file "REGISTER.FRM", fill
  it and send to this address:

                   Martin Mal¡k
                   Jakubovo n m. 3
                   811 09 Bratislava
                   SLOVAK REPUBLIC
                   EUROPE

  If you include your Internet e-mail address, you will receive the keys via
  e-mail, otherwise snail mail.

  Once you have obtained the five Keys needed to register, put exactly the same
  name (as included in REGISTER.FRM), all keys in the [Register] menu of HWiNFO
  and the current version will become registered.

  Note: Remember the name string, you've send me in REGISTER.FRM, because the
        Registration Keys depend on it !


  Well, the Registration fee is:
 
  Single Registration                  -> 20 DEM / $15
                                          or 300.- Sk/KC (Slovak/Czech people)

  Multiple Registrations (Companies)   -> Contact me first for special
                                          arrangements.

  A registration is valid for all future versions. And there will be a lot of
  newer versions of course.

  You should register Now !








 ## Comments... ###############################################################


  The CPU ID is available only on 386+ CPUs and HWiNFO uses three ways to
  obtain this ID:

  Method 1 - Does Reset the CPU while A20 is Enabled.
             This method works on all systems, but the Reset handler gets
             control after BIOS. And some BIOSes (some newer AMI/Award BIOSes)
             destroy CPU ID (EDX) and therefore this ID could be invalid.
             This method is default <Enabled> in Setup section.

  Method 2 - Does Reset the CPU while A20 is Disabled.
             This method works only on some machines, which do have a
             Fully-Terminated bus. It's a better way to obtain CPU ID, because
             it gets control immediately after Reset (the BIOS can't destroy
             EDX).
             This method is default <Disabled> in Setup section.

  Method 3 - Try to use this method if your BIOS destroys CPU ID. But it works
             only on systems, which do not have Main BIOS Write-Protected,
             because it modifies it for a bit, and then restores back. (This
             method works well on my machine and is the only way to get CPU ID).
             This method is default <Enabled> in Setup setction.



  HWiNFO tries to determine CPU ID this way, via: 1. CPUID instruction
                                                  2. BIOS (INT 15h)
                                                  3. Method 2 (if Enabled)
                                                  4. Method 3
                                                  5. Method 1

  If you have an UMC U5SX/SD/SLV/486DX2/SX2, Enhanced Am486DX2/DX4/DX4-WB,
  Intel 486DX/SX/DX2 SL-Enhanced, IntelDX4, IntelSX2, IntelDX2 W-B Enh. or
  Intel Pentium(TM) and above, there is no need to Reset the CPU (these CPU
  support CPUID instruction). The most CPUs today support CPUID instruction.
  Note: Nx586 and Cyrix 5x86 do NOT support CPUID instruction yet.

  Disabling "CPU ID detection via Method 1, 2 and 3" reduces your CPU detection
  range ! And if there's no other way to obtain this ID (via BIOS or CPUID
  instruction), it won't identify 386SL, i386CX/EX, 486DX2, IBM 486... and some
  other CPUs. Do this only if your system hangs while CPU detection.

  Some BIOSes (like - AMI PCI PnP WinBIOS 12/15/93) simply OVERWRITE the
  CPU ID (EDX) :-< ! In this case is an invalid CPU ID displayed and the CPU
  problably not correctly identified. If this problem occurs, try to use
  Method 3 (but your Main BIOS must be Write-Enabled !). If it doesn't work,
  try to use Method 2 (but you must have a Fully-Terminated bus !). And if
  HWiNFO still displays, that Method 1 was used to obtain CPU ID, not Method 2
  nor 3 can obtain it.





  ARIA sound card, Stacker Compression Card and 3Com EtherLink III Adapter
  detection routines cause crash with some Network cards. You can disable them
  the in Setup section (ARIA and Stacker check are default disabled;
  3Com EtherLink III detection is enabled).


  On some old motherboards are random number obtained from not used I/O ports
  and this may cause invalid identification of Aria sound card or Hitachi
  CD-ROM. I don't know how to solve this problem.


  The Mainboard Chipset indentification works only on newer (÷ 1991 and above)
  AMI and newer AWARD BIOSes.
  HWiNFO is also able to detect: û  Intel 82420TX SATURN
                                    Intel 82420EX ARIES
                                    Intel 82430LX MERCURY
                                 û  Intel 82430NX NEPTUNE
                                 û  Intel 82430FX TRITON
                                 û  Intel 82430HX TRITON II
                                 û  Intel 82430VX TRITON II
                                 û  Intel 82430MX MOBILE TRITON
                                    Intel 82440FX NATOMA
                                 û  Intel 82450KX/GX ORION
  chipsets, not depending on the type of BIOS.


  Fixed Disk Data Transfer rate reads data from one physical sector until 4
  secconds. Some caches (like Hyperdisk; but NCACHE or SMARTDRV don't) could
  cause invalid results. Also some mainboards, which have incompatible
  timers could cause problems.


  Fixed Disk Average Seek receives results while seeking permanently 100* from
  cylinder 0 to a cylinder, which is 1/3 of the max. cylinder number. Thus some
  programs could report another results if they seek to an another cylinder.
  SCSI disks and some Cache programs (Hyperdisk) don't generate Seek requests,
  thus the Seek and RPM result is abnormal and HWiNFO displays <N/A>.


  PCMCIA detection requires Socket Services to be installed.


  Video Throughput benchmark depends only on External CPU frequency and the
  type of Video board used; e.g. 486DX-33 with the same graphics board as an
  i486DX4-100 (running at 3*33 MHz) report the same Video Throughput speed !


  CD-ROM benchmark requires MSCDEX.EXE (Microsoft CD-ROM Extensions) to
  be installed.


  The Internal (1st level) Cache size reflects only Data cache. This means,
  that it gives real results on 486- systems, but on Pentium+ systems, which
  have separate caches for Data and Instructions, it returns only the size of
  Data cache. Maybe in the future I'll add a test for both parts. Intel
  Pentium Pro and above directly return information about TLB (Translation
  Look-aside Buffer), Level 1 and Level 2 on-chip caches -- info about TLB is
  displayed in CPU Identification section and L1, L2 cache implemented into
  System info.


  Intel Pentium and above CPUs do not report, that the "APIC on-chip" feature
  is present. They do have an Advanced Programmmable Interrupt Controller
  on-chip, but don't report it, if it isn't supported by external hardware.


  Dhrystone benchmark tests the performance of CPU and Memory, but only in
  16-bit code. And so, a 150 MHz Pentium Pro (which is designed and tuned
  especially for 32-bit code) returns a rather low Dhrystone result.
  So, it's performance while running with 16-bit applications is comparable
  to a 100 MHz Pentium P54C.


  If you have an Intel TRITON FX/HX/VX/MX or SiS 85C511 chipset, HWiNFO is
  able to detect the Type of External Cache and it's size directly from the
  chipset registers. The possible types are:
   û  Synchronous Pipelined Burst Cache
      Synchronous Burst Cache
   û  Asynchronous SRAM Cache
      Dual-Bank Pipelined Burst Cache
  Also if you have an Intel TRITON FX/HX/VX/MX chipset, HWiNFO is able to
  detect if you have EDO RAM.


  HWiNFO is able to detect these types of Video RAM:
   û  EDO DRAM/VRAM - for S3 chipsets
   û  WRAM - for Matrox MGA Millennium board
      SDRAM - (Synchronous DRAM) for Cirrus chipsets (CL-GD5480)
      RDRAM - (Rambus DRAM) for Cirrus chipsets (CL-GD546x)







  ## Running under V86 Memory Managers #######################################

  HWiNFO (v3.00+) is able to run in Virtual86 mode under some circumstances
  (it means, under some applications, which turn the V86 mode on). But ONLY
  those, which support the Windows INIT BROADCAST and handle it correct. Such
  known applications are:
   - Microsoft EMM386 Expanded Memory Manager
   - Quarterdeck QEMM386 Expanded Memory Manager
   - Qualitas 386MAX Expanded Memory Manager
   - Nu-Mega Soft-ICE Debugger
   .......

  These applications are able to switch to Real mode when they receive the
  Windows INIT BROADCAST. But if you run HWiNFO in V86 there may occur some
  problems, especially during CPU RESET (like hang, crash...). Also some
  Memory Managers, which relocate BIOSes may cause misidentification of BIOS
  (like QEMM386's Stealth Mode). HWiNFO works best under EMM386 (I didn't find
  any problems).
  The method of detecting CPU frequency via TSC (Time Stamp Counter) doesn't
  work if V86 mode is turned on.
  <<< So, I prefer to run HWiNFO in Real Mode. >>>

  HWiNFO is unable to run under Microsoft Windows, Windows95, Windows NT and 
  OS/2, because they don't switch to Real Mode and also manipulate Benchmark
  results, BIOS scan, are able to control direct I/O operations, which can
  cause invalid results and Windows NT doesn't allow 16-bit appz to directly
  access the disk and some hardware routines cause problems, thus it can't be
  supported.



 ## Seccond Graphics Accelerator ##############################################

  RISC Graphics Processor: currently identifies only Hitachi HD63484 ACRTC
  Scanning for TMS: checks for TMS340x0 processor on several ports and tries
                    to get vendor and device name (detection routine from
                    SPEA GDC drivers, I don't know if it works with other
                    cards too)
  TMS Boot EEPROM: gets info from Boot Software; this won't probably work
                   with other cards than SPEA (I don't know :-( )
  TIGA driver: gets info from TIGA driver if it's loaded (TIGACD.EXE)
  Also found as: identifies all SPEA Graphiti series cards from GDCINI.DAT
                 and checks for HP IGC-20 and NEC MultiSync Graphics Engine

  You can obtain info such as:

  e.g.: RISC Graphics Processor:   Hitachi HD63484 (ACRTC)
        Scanning for TMS:          N/A
        TMS Boot EEPROM:           N/A
        TIGA driver:               N/A
        Also found as:             SPEA Graphiti Flash 1G2-HE

  or:   RISC Graphics Processor:   N/A
        Scanning for TMS:          (C) SPEA Software AG HILITE1024
        TMS Boot EEPROM:           SPEA HiLite1024 
        TIGA driver:               N/A
        Also found as:             SPEA Graphiti HiLite1024

  or:   RISC Graphics Processor:   N/A
        Scanning for TMS:          <I really don't know what it'll display>
        TMS Boot EEPROM:                             -||-
        TIGA driver:               HP A1083A Intelligent Graphics Controller 20
        Also found as:             Hewlett Packard IGC-20 A1083A








 ## Creating a logfile ########################################################

  You can create a log-file by pressing the <PrintScreen> key; it will add the
  results from current screen to a file named "hwinfo.log". You can change the
  name of this file by entering the .log filename you want, as an paramater to
  hwinfo; e.g. "hwinfo.exe my_p7.log".

  There is also an Auto-Logging feature, that automatically logs all screens,
  which you open. You can enable it in the Setup menu.









 ## Thanx #####################################################################

 I want especially thank to:

 ù Beta testers: Boris Hur¡nek; bhurinek@axa.sk
                 Erik Francisci; franto@iris.elf.stuba.sk
                 Igor Junas; junas@isnet.sk
                 Mat£s Rosa; rosa@elf.stuba.sk
                 Milan Marusinec; marusine@ba-cvt.sanet.sk
 ù Alex V. Potemkin and Potemkin's Hackers Group; root@chaos.remote.misa.ac.ru
 ù Aad Offerman (CHIPLIST); offerman@einstein.et.tudelft.nl
 ù J n G£cik (IntroScope - a pretty good prg); jan.gucik@vslib.cz
 ù Jeremy Lilley (PROTECT! -ion); 75060.2074@compuserve.com
 ù Tom s Lehuta (GUS Memory routs); lehuta@elf.stuba.sk
 ù Peter Hubinsky (SAC fileadmin); hubak@elf.stuba.sk
 ù Emil Laurentiu (hints); lcarmen@u1.ici.ro






 ## Disclaimer ################################################################

 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º  All product names are copyright and registered trademarks/tradenames of   º
 º                        their respective owners.                            º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

           HWiNFO IS COPYRIGHTED MATERIAL AND PROTECTED BY APPLICABLE
               COPYRIGHT LAWS AND INTERNATIONAL TREATY PROVISIONS.


    THE PROGRAM AND ITS DOCUMENTATION ARE COPYRIGHTED BY THE ORIGINAL
    PROGRAMMER/AUTHOR (COPYRIGHT HOLDER). ALL RIGHTS ARE RESERVED CONCERNING
    FUTURE CHANGES OF THE NAME AND CONTENTS OF THIS DISTRIBUTION PACKAGE. NO
    CHANGES MUST BE MADE FOR ANY REASONS AT ANY TIME BY ANYBODY IN ANY ASPECT,
    INCLUDING, BUT NOT LIMITED TO, MODIFICATION OF THE COPYRIGHT NOTICE OR
    CHANGES OF THE COMPILED BINARIES HEREBY ALTERING THE ORIGINALLY INTENDED
    PROGRAM EXECUTION FLOW.

    RealSoft SPECIFICALLY DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, AND
    ALL LIABILITY, INCLUDING CONSEQUENTIAL AND OTHER INDIRECT DAMAGES, FOR
    THE USE OF THIS SOFTWARE, INCLUDING LIABILITY FOR INFRINGEMENT OF ANY
    PROPRIETARY RIGHTS. RealSoft DOES NOT ASSUME ANY RESPONSIBILITY FOR ANY
    ERRORS WHICH MAY APPEAR IN THIS CODE NOR ANY RESPONSIBILITY TO UPDATE IT.

    THE PERSON USING THE SOFTWARE BEARS ALL RISKS AS TO THE QUALITY AND
    PERFORMANCE OF THIS SOFTWARE.



1 ## END #######################################################################