AT3  ---  by Rob Hamerling

    AT3

    This document describes the program AT3 for OS/2 2.0 and up (32-bit
    version).


    INTRODUCTION

    AT3 is a simple OS/2 program with a limited but useful function: it
    sends characters from the OS/2 commandline as AT-command to a Hayes
    compatible modem (with blanks suppressed).

    AT3 also shows the modem response(s), if any, which may be redirected,
    for example to be stored in a file.


    WHO MAY USE AT3?

    AT3 may be used for private personal use only, not in a commercial or
    business environment.  Please contact the author if you have a business
    need for AT3.

       R. Hamerling
       Vianen, The Netherlands
       Phone: BBS/FAX: 31-347-322423
       FIDOnet: 2:281/732 or 2:280/804.1098
       E-mail: rob.hamerling@f732.n281.z2.elcom.org

    AT3 may be distributed freely, without charging a fee, as long as it
    remains a complete package as originally distributed and no other
    changes are applied without the explicit permission by the author.


    PACKAGE CONTENTS:

    AT3 is distributed as ZIP file (AT3_15B.ZIP) with the following
    contents:

    AT3.DOC   This documentation file

    AT3.EXE   32-bits executable, for OS/2 2.0 and newer

    IBM7855A.CMD Sample commandfile to customise an IBM 7855-010 modem for
              use in ASYNC mode with RTS/CTS handshaking.



    AT3 PARAMETERS

    AT3 builds the string to be sent to the modem with all commandline
    parameters.  These may be specified as a single string, or as separate
    parameters, which will be concatenated by AT3 to form a single string.
    The string will be preceeded with 'AT' and terminated with a Carrier
    Return character (ASCII 13).

    The string will be sent to the modem in 8-bit, NO parity, 1 stop-bit
    mode.

    
                                                                     AT3  1


                          AT3  ---  by Rob Hamerling



    SPECIAL PARAMETERS

    AT3 accepts 2 optional parameters to control its behaviour.  These must
    be specified as first parameters on the OS/2 commandline and can only
    be numeric to distinguish them from modem-commands.  Of course these
    parameters will not be sent to the modem, AT3 will send the first
    non-numeric and all subsequent parameters (even if numeric) to the
    modem.

    1. A value from 1 to 8 will be considered as port number (COM1...COM8).
       COM1 will be addressed by default.

    2. A value higher than 8 will be considered as port-speed to be set and
       subsequently used to transmit the AT-command and receive the modem
       response.  If not specified, the speed with which the COM-port has
       been initialised before will be used and not changed.

    When either the port is not available (not installed or in use), or the
    speed is not an acceptable value for OS/2, AT3 will terminate with an
    error message, and not issue an AT-command.  The most common errors
    are:

    þ  Invalid port number will result in a DosOpen failure (rc=110)
    þ  Unacceptable speed will give a DosDevIOCtl error (rc=87)

    AT3 does not perform any kind of syntax checking for modem commands.


    EXAMPLES

    Here some examples for AT3:

    AT3 Z          Reset modem: AT3 will send 'ATZ<CR>' to the modem.

    AT3 E1         Set modem command-echoing ON: AT3 will send 'ATE1<CR>'
                   to the modem.

    AT3 19200 M1   Set the com-port to 19200 bps and set modem-speaker on.

    AT3 2 \S       Report configuration of modem on COM2.

    AT3 ^&V >modem.cfg Report current and stored modem profiles, and store
                   modem responses in file 'modem.cfg' (this command may
                   vary with the modem).

                   Note: A '^'-character is needed as escape-character in
                   front of every '&'-character on the commandline of AT3!
                   The '&'-character otherwise acts as command separator.
                   See your OS/2 command reference manual for details.

    AT3 ^&Z0=322423 Store (replace) a telephone number in the modem
                   directory.

    Of course these are just examples, use your imagination and your modem
    manual!

    
                                                                     AT3  2


                          AT3  ---  by Rob Hamerling



    COMMANDFILE FOR IBM7855

    Of course AT3 can also be used from a batch file or a REXX procedure.
    As an example this AT3 package contains a file IBM7855A.CMD to
    customise the IBM 7855-010 modem for use by an asynchronous
    communications package.

    With a slight modification (&M2 in stead of &M0) the modem is
    started-up in sync-mode with power-on.  So the modem can be used with
    the communications manager in SDLC-mode with a Multiprotocol
    Communications Adapter or SDLC-card, and be used in Asynchronous mode
    after switching the modem to an Asynchronous communications port.


    RETURNCODES

    When encountering some kind of problem during execution, AT3 displays a
    message indicating the last executed Function (DosOpen, DosDevIOCtl,
    etc), and the returncode of that function.  This returncode is also
    returned in 'errorlevel' for use in batch files.

    When AT3 is invoked without any parameter, some help information is
    displayed, and a returncode of 1 is returned.

    When the modem does not respond, the returncode of AT3 will be the
    value 255.  This may however not be a real error. Examples are: the
    modem is in echo-off state, programmed to not responding.





























    
                                                                     AT3  3


                          AT3  ---  by Rob Hamerling

    IMPLEMENTATION



    IMPLEMENTATION

    AT3 is completely written in C-language, and uses the standard OS/2
    Application Programmers Interface and functions provided by the
    COM-port driver COM.SYS for OS/2 2.0 and newer.  The program has been
    compiled with IBM C/C++ 2.0 and IBM Program Development Toolkit for
    OS/2 Warp.


    CONTROL OF THE DTR SIGNAL

    AT3 does not set DTR true during execution by default.  The reason for
    this is that modems which are programmed with a phone number to be
    dialed when DTR becomes true might inadvertently start to dial that
    number when AT3 only tries to deliver an AT command.  On the other hand
    there are modems which do not accept an AT command when DTR is not
    true, and almost certainly will not deliver responses in that case.

    To make AT3 generally useful for modems which require DTR being true
    before accepting AT-commands, AT3 scans for the environmentstring "AT3"
    during at startup.  When this string is set to "DTR", AT3 activates the
    DTR lead before delivering its AT-command, and drops it at termination.
    Otherwise AT3 keeps DTR false.

    So enter (e.g. in your CONFIG.SYS):

         SET AT3=DTR

    in case you have a modem that needs DTR to work with AT3.  If you don't
    know, just try without this SET command to see if AT3 works as desired.
    If not then make it work with this enviroment setting.

    Note: AT3 makes RTS true during execution, otherwise hardly any modem
    would listen to commands from the computer.


    DIALING

    If you want to use AT3 for dial commands, then you need to set the
    environment variable slightly different, for example:

         SET AT3=DTR,500

    Hardly any modem will execute a dial-command whithout DTR being true.
    But also the standard timeout of AT3 is too short to wait for the
    completion of a dial command.  DTR will be turned off after that time,
    which will prevent the modem from finishing the dial operation.  The
    sample value of '500' modifies the standard timeout from .5 seconds to
    5 seconds (the value is expressed in hundredths of seconds), which will
    generally be large enough for tone-dialing.  But it may not be the
    right value for your modem, modem command or network.  Experiment with
    this value!


    
                                                          Implementation  4


                          AT3  ---  by Rob Hamerling

    Note: Only values higher than the default of 50 (.5 seconds) are
    accepted.


    LIMITATIONS

    The following minor restrictions may cause you some inconvenience:

    þ  Most Hayes-compatible modems have a commandbuffer of 40 characters.
       Therefore AT3 limits the command-string to 40 characters.
       '^'-characters on the commandline do not appear to AT3 and will
       therefore not be included.  The first parameter that would make the
       length of the AT-command string exceed 40 characters and all
       subsequent parameters will be ignored.  Of course this does NOT
       include AT3-parameters for COM-port and speed.  If you need to sent
       more data to your modem, use as many invocations of AT3 as you
       desire.

    þ  For communication with the modem, AT3 may change certain COM-port
       parameter settings.  These parameters are not reset to their
       previous values after AT3 has finished.  This may leave the port in
       a setting that you may want differently.

    Always issue a MODE command with the proper parameters after using AT3.


    AT3 IS NOT A REPLACEMENT FOR MODE

    AT3 is not a stand-in for the MODE command:

    þ  It would make AT3 considerably more complicated and error-prone.
    þ  Every OS/2 installation has the MODE-command available, so why
       duplicate good work?

    The exception is the setting of port-speed.  Using the MODE-command
    just for setting the speed of the COM-port has the potential problem
    that it may set DTR true.

    Use AT3 to address your modem, use MODE to control your COM-port.


    AT3 DESIGN ISSUES

    It was originally designed for just switching a modem from SYNC to
    ASYNC mode (and vice versa) in a situation where communications
    services are used of which some use Synchronous (SDLC) protocol and
    others use Asynchronous protocol.  This could be done with redirecting
    an ECHO command (ECHO ATE1 >COM1), which works perfectly for DOS in
    combination with some modems.  However, OS/2 and some other modems
    behave differently.

    MODE and ECHO may result in DTR becoming true (and may stay true!).
    And the modem might be programmed to dial a built-in phone number to a
    SYNC connection point when DTR becomes true.  This may have some
    undesirable effects:

    þ  It is in most cases not useful to start dialing the programmed

    
                                                          Implementation  5


                          AT3  ---  by Rob Hamerling

       number when you are in the process of configuring your COM-port or
       modem.
    þ  It is certainly not useful to dial a service with Synchronous
       protocol when the modem is connected to an ASYNC port (which is the
       only possibility to deliver AT-commands)!

    To avoid these problems, AT3 opens the COM-port by default without
    making DTR true

    With AT3 you must be able to send any AT-string to the modem.  To avoid
    a possible interpretation error (whether AT3 should use a commandline
    parameter as program-parameter or a modem-command), an environment
    variable is used to control the DTR signal.

    AT3 waits about 0.5 seconds for the modem to transfer a response after
    receiving an AT command.  This timeout is long enough for most modems.
    On the other hand it ensures that AT3 terminates quickly when there is
    no response, or even when there is no modem connected to the port at
    all.

    Some modems have multiple output screens to show its configuration
    after being requested so (for example with the command AT\S).  The
    operator is requested to hit the ENTER key before the modem shows the
    next screen of information.  AT3 tries to anticipate this situation by
    issuing a CR (Carriage Return) when the modem stops sending data.  If
    this works for your modem you'll get the modem-configuration in 1
    single outputstream.  Otherwise you may get the remaining screens at
    the next occasion, for example when your 'real' communications program
    opens the COM-port.





























    
                                                          Implementation  6


                          AT3  ---  by Rob Hamerling

    APPENDIX A.  SAMPLE REXX COMMANDFILE FOR SETUP OF IBM 7855 MODEM

    /* ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»        */
    /* º  IBM7855A.CMD by Rob Hamerling (see AT3.DOC file).  º        */
    /* ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼        */
    /* Change portnumber into the appropriate value (2 for COM2 etc). */
    /* Change phone number as desired.                                */

    modem = 'IBM 7855-010'
    port  = '2'
    speed = '19200'
    phone = '322423'

    Say ''
    Say 'Customise 'modem' modem for ASYNC (put it in SYNC mode with &M2).'
    Say 'Modem must have been set in AT-commandset mode from the frontpanel!'
    say ''
    say 'Modem is supposed to be on COM'port':'

    set AT3'='

    /* First see if the modem responds: */
    AT3  port  speed  'I'
    if rc > 0 then signal noreply

    /* Reset the modem to the factory settings: */
    AT3  port  '^&F1'
    if rc > 0 then signal problem

    /* Transmit the customisation commands: */
    /* (this may be a little bit more than absolutely needed after &F1) */
    AT3 port 'B0 E0 L1 M0 Q0 V1 X4 S0=0'
    AT3 port '^&AP7 ^&AL8 ^&B8N1 ^&C1 ^&D2 ^&I0 ^&L0 ^&M0 ^&R1 ^&S2 ^&X0 ^&Y0'
    AT3 port '^\A3 ^\C3 ^\G0 ^\K2 ^\M14 ^\N3 ^\Q2 ^\R2 ^\T2 ^\V1 ^\X0'
    AT3 port '%%B0 %%C0 %%D0 %%E1 %%F1 %%G1 %%H1 %%I1 %%O1 %%R1 %%V0'

    /* Store current configuration to both(!) NVM profiles */
    AT3  port  '^&W0 ^&W1'

    /* Finally set the phone number to be auto-dialed in SYNC-mode. */
    AT3  port  '^&Z'phone

    exit 0

    problem:
    if rc>0 then Say 'See returncode of reported function for probable cause.'

    noreply:
    if rc=255 then say '[rc='rc'] Is 'modme' modem connected to COM'port'?'
    exit rc








    
        Appendix A.  Sample REXX commandfile for setup of IBM 7855 modem  7