(C) 1994  T.C. Green, PEng (t.green@ieee.org)

EXCON -- direct control of X10 events via CP-290


Syntax:

        excon [c=config] [+colour|+mono] [-mouse] [p=comport]
                [h=house_code] [u=unit_code] [i=intensity] [all] 
                [lights] [house_code|unit_code|both_code] 
                [on|off|dim|fade]


Options:

        c=      specify the name of the configuration file
                (default is EX10.CFG in the current directory, or
                if this fails, EX10.CFG in the directory from
                which EX10.EXE was executed).  This configuration 
                file is the same used by the EX10 program.

        +c      override the screen colours specified in the
                configuration file with the default set for a
                colour screen

        h=      house code used in direct command mode (default 
                is "h=A"), in range A to P

        i=      intensity used in direct command mode, 
                percentage in range 0 (full off) to 100 (full on)

        +m      override the screen colours specified in the
                configuration file with a default set visible on a
                monochrome screen

        -m      assume there is no mouse (default is to assume
                there is a mouse and complain if it can't be
                found).  This means that the mouse cannot be used
                to control the program.

        p=      override the comport specified in the
                configuration file (if any).  If there is no
                configuration file, and the "p=" option is not
                used, p=2 is assumed (interface on COM2).  COM1
                through COM4 (p=1 through p=4) are supported.

        u=      unit code used in direct command mode, in range 
                1 to 16

        lights  direct mode command applies to lights only

        all     direct mode command applies to all units (or 
                possibly all lights if "lights" is given)

        on      turn specified unit(s) on; direct mode

        off     turn specfied units(s) off; direct mode

        dim     turn specified units down to specfied intensity;
                direct mode (only works for lamp modules that can 
                be dimmed) 

        fade    dim units down to zero intensity if they are lamp 
                modules, or turn them off if they are not; direct 
                mode

        house_code  house code will apply to all unit codes that 
                follow it, for specifying direct mode command 
                (same has "h=")

        unit_code  unit code to specify which unit will respond 
                to direct mode command (same as "u=")

        both_code  house code and unit code (e.g. A12) of units to 
                be controlled by direct mode command

Examples:

        excon
        excon A10 off
        excon A10 A12 i=50 dim
        excon D all off


Description:

EXCON is a companion program to EX10 and shares a common 
configuration file.  It requires a CP-290 to work.  It has an 
interactive mode (invoke without direct command mode arguments) 
arguments as in the first example) for which the interface is 
much like that of EX10.  Read the documentation for EX10 first. 

EXCON can also issue X10 commands throught the CP-290 to 
specified units.  Units to be controlled can be specified with 
explicit house and unit code arguments (e.g. "h=", "u=") or with 
the combined form (e.g. A12 or P2).  Units can also be specified 
as "all" meaning all units for the specified house code, or as 
"lights" (usually "all lights").  Multiple units for a single 
house code can be controlled in a single command.

EXCON actions include "off" (turn specified units off), "on" 
(turn specified units on), "dim" (dim dimmable units to the 
intensity previously specified with the "i=" argument) and "fade" 
(uses an undocumented feature in the CP-290, and may not work in 
all situations).  Using "all lights" may not work properly in all 
situations either since it also uses an undocumented feature.


Limitations: 

There can only be one action for each command line in direct 
command mode; only the last command found as the command line is 
parsed left to right will be executed.  For example, the following 
will not work properly:

        excon A10 on A12 off

Units for only a single house code can be controlled in a single 
direct mode command.  For example the following will not turn 
both A10 and B12 off:

        excon A10 B12 off