Loading the ODI drivers at an interrupt other than 60.

  ODIPKT # int
         |  |
         |  +-- desired interrupt vector, in decimal (e.g.,
         |      0x60h=96, 0x65h=101
         |
         +----- logical board number (determined via NET.CFG),
                one of 0,1,2 or 3.

E.g., You have an SMC Ethercard Elite, want to use interrupt 62 (hex)
and the following NET.CFG:

  link driver SMCPLUS
     port 240
     frame Ethernet_802.3
     frame Ethernet_II
     [...]

You would load ODIPKT thus:

  ODIPKT 1 98

You specify logical board 1, because in your NET.CFG, Ethernet_II is
set-up as the second logical network board (Ethernet_802.3 is the
first logical board).  If you're only using Ethernet_II packets, you
specify logical board 0.-- 


_________________________________________________________________________
RUCS     | Mark A. Medici, Systems Programmer III, User Services Division
User     | Rutgers University Computing Services, New Brunswick, NJ 08903
Services | [medici@gandalf.rutgers.edu]                    [908-932-2412]