Fsend Version x.yy
                              Reference Manual










           Created 1992 - 1997 by Dr. Harald Pollack & Bernhard Seidl






-------------------------------------------------------------------------------
    ABBREVIATIONS USED IN THIS DOCUMENTATION
-------------------------------------------------------------------------------

    DTE . . . . . . . . . . Data Terminal Equipment, your PC
    DCE . . . . . . . . . . Data Communication Equipment, your MODEM

    CCITT/ITU T.4 . . . . . International standard for coding fax data.
    CCITT/ITU T.30  . . . . International standard for transmitting fax over
                            a public switched telephone network.

    ANSI/EIA/TIA-578-1990 . Asynchronous Facsimile DCE Control Standard
                            Service Class I (the common used class 1).

    ANSI/TIA/EIA-592-1993 . Asynchronous Facsimile DCE Control Standard
                            Service Class II (the real class 2.0).



-------------------------------------------------------------------------------
    WARRANTY
-------------------------------------------------------------------------------

    There is no warranty on this program. You can use it for your own risk.
    The program should work the best way it can. If you detect some
    malefunction or bugs, please report it with the correspondent FSEND.DEB
    log file to the autor. Without the log file it is almost inpossible to
    find and fix a bug. Common bugs will be corrected if they are of vital
    interrest to the program. Wishes for some extentions (but not printing
    and viewing) and hints for making things better are welcome.




-------------------------------------------------------------------------------
    UPGRADING TO A NEW VERSION
-------------------------------------------------------------------------------

    New versions of Fsend are always packed in LZH type archives. It is
    recommended to replace all EXE and DLL files and not to use parts of
    older version (especially DLL files). New versions of Fsend often use
    new or modified configuration entries and commandline options. Please
    read all available documentation carefully before using a new version.



-------------------------------------------------------------------------------
    THE CONFIGURATION FILE
-------------------------------------------------------------------------------

    The configuration file keeps all information required. FSEND.CFG needs
    to be modified to suit your system. Please have a look at the sample
    configuration file included in the Fsend package. In the following
    section all keywords and parameters are listed and described.


    NOLOGONBAD
        If Fsend is used in conjunction with third party environment (e.g.
        FaxWorks*, see also FAXLOG and FAXIDX keywords) and this keyword
        is used, no log entry will be generated if there occured an error
        while receiving or no fax session was established. Also see '-#'
        command line parameter.

    [TASK <n>]
        Starts a section within the configuration file which only effects
        the selected task. To end a section you can either use another
        [TASK <n>] keyword which would start another section or use the
        keyword [CONNON], described below.

    [COMMON]
        All keywords after this statement belong to all tasks.

    CONFIGEND
        Fsend will stop working off the configuration file and everything
        following this keyword will be ignored.

    KEYFILE <file name>
        The name of a key file which will be used in future versions for
        registration details.

    LOGBINKLEYSTYLE
        Using this keyword Fsend will generate BinkleyTerm like log entries.

    USROBOTICS
        Special keyword to indicate that a USRobotics modem is used. Must
        be set to allow some workarounds for nonstandardized actions!

    OLDDTR
        Fsend uses the methode of 'DTR-drop' (switching modemline DTR off
        and on) to reset the modem and to force a on-hook condition. This
        switching might be done in two ways (different calls to DosDevIOCtl).

    NOHEADERLINE
        Default a header line is created on the top of each fax page
        containing date, time and some other informations . To disable
        the creation of that line you have to use 'NOHEADERLINE' keyword.

    NOFOOTERLINE
        Default a footer line is created on the bottom of each fax page
        containing the name of recepient (also see '-d' command line parameter)
        and the dialed fax number. To disable the creation of that line you
        have to use 'NOFOOTERLINE' keyword.

    NOGARBAGE
        Some older fax modems echo the fax data sent to DCE back to DTE. To
        suppress the logging of all this 'garbage', use this keyword.

    NOEOM
        This keyword disables the standardized behavior of Fsend.
        Fax machines, some class 2 and 2.0 fax modem and a minority of class 1
        fax receive software will treat this ITU-T.30 command in a correct
        manner,  but the majority of fax modem and software can not handle this
        command and may malefunction or even hang. Alternativly, the '-noeom'
        command line parameter can be used.

    TEXTCOLOR <colorvalue>
        Select color of characters on Fsend status screen:
            0 . . . BLACK
            1 . . . BLUE
            2 . . . GREEN
            3 . . . CYAN
            4 . . . RED
            5 . . . MAGENTA
            6 . . . BROWN
            7 . . . LIGHTGRAY
            8 . . . DARKGRAY
            9 . . . LIGHTBLUE
            10  . . LIGHTGREEN
            11  . . LIGHTCYAN
            12  . . LIGHTRED
            13  . . LIGHTMAGENTA
            14  . . YELLOW
            15  . . WHITE

    TEXTBACKGROUNDCOLOR <colorvalue>
        Select color of background on Fsend status screen.

    FRAMECOLOR <colorvalue>
        Select color of the frame on Fsend status screen.

    TEXTEXTENSION <file extension>
        Fsend uses the extension of a file to determine the method for
        conversation. Default Fsend assumes a file has Tiff format. But
        there are some exceptions. Bitmap files will be treated correctly
        if '.BMP' extension is used. Plane ASCII text files also will be
        treated correctly if '.TXT' extention is used. To determine more
        extentions for text files 'TEXTEXTENSION' can be used.

    SENDBUFFER <buffer size>
        Default a buffer of 1024 bytes is used to transmit portions of fax
        data from DTE to DCE. This buffer is used only partially. In worst
        case half of the buffer is filled with data. To optimize transmitting,
        default 8 buffers are used. The buffer size can be determined through
        'SENDBUFFER' keyword. 64 to 4096 bytes are valid buffer sizes.
        Note: The number of buffers is adjusted automatically to have a
        minimum of 4 buffer or 8192 bytes overall size.

        Attention: The default values (8 x 1024 bytes) yields in best
        performance and less need of resources. Increasing the size may
        result misbehavior, especially if a rather slow bit rate are used
        at fax negotiation! Buffer size may be decreased if your PC has
        excellent IO-performance (less IO waitstates from mainboard design)
        which yields in less needs for system resources. Do not change the
        buffersize, if using class 1!

    RESET <modem command>
        The first action after start up of Fsend is to set the baud rate you
        have determined using 'DATABAUDRATE' keyword. The modem command
        defined with 'RESET' will be sent to DCE after setting the baud rate.
        Attention: At least 'AT' is required for that the modem to detect the
        change of baud rate! But it is recommended to use a modem command
        which resets the modem (e.g. 'ATZ').

    DIAL <dial command>
        Default, 'ATD' is used. If an other dial command is required (e.g.
        'ATD0W') 'DIAL' keyword can be used.

    INIT <modem command>
        Default no init commands are used by Fsend. Read the sample
        configuration file for fax service class depending additional
        required or useful commands. Do not use any resetting command
        like 'ATZ' or 'AT&F'!

    FAXCLASS <1 or 2 or 2.0>
        Select a fax class, your modem is able to handle. Fsend supports
        fax calss 1, class 2 and class 2.0.
        Note: Only class 1 and class 2.0 are standardized! There is no
        general valid standard for class 2.

    CLEANUP <modem command>
        Recommanded is at least 'AT', but you can use any modem command.

    LOCALPHONE <phone number>
        Your voice phone number. For informational purposes only.
        The phone number will be shown in cover page.

    LOCALNAME <your name>
        Will also only be used for informational purposes on cover page.

    LOCALID <fax number>
        This value is used to generate the TSI frame. Only use '+', ' ' and
        '0' - '9' characters (as defined in ITU-T.30). All other alphanumerical
        information is not standardized (and therefor discarded).

        Attention: This parameter is mandatory, Fsend is stopped if not
        defined!

    STATIONID <your company or elsewhat>
        This information is only transmitted, if faxmodem is able to handle
        NSF (NonStandardFacility) frames. Usualy, class 1 modems can do it.

    FAXPATH <path>

        This entry is MANDATORY!

		Defines the path to a directory where fax files are situated and
		ready to send (e.g. 'X:\FAX\'). Also see '-#' command line parameter.
		FAXPATH is also used to form a fully quallyfied path to FAXLOG and
		FAXIDX.

		Additional parameters as used for FREC (like SUB and PWD) are ignored.

	FAXLOG <file name>
		Filename to FAX.LOG and only neccessary, if other than
		'FAX.LOG'. Received faxes from FREC will be joined to FAX.LOG.
		Each well received fax (hangup code 0) is flagged as 'Rcvd'. If fax is
		received in (partial) error or even no session was established at all,
		entry in FAXLOG is flagged as 'BadRcv'. See also keyword NOLOGONBAD.
		Also see '-#' and '-FaxLog' command line parameter.

	FAXIDX <file name>
		Filename to FAX.IDX and only neccessary, if other than
		'FAX.IDX'. Also see '-#' command line parameter.

    FAXDEBUG <[+]file name>
        This is the name of the log and debug log file of Fsend. Nearly all
        activities are stored in this file. If a '+' precedes the path,
        append mode is used: one log is chained to the next. Select NUL as
        filename to disable logging.
        The logfile contains a lot of informations in case of errors or
        situations where help is needed. Bugreports to the author are only
        sensful if this logfile is part of the report.

    FAXBAUDRATE <DTE-DCE bit rate>
        Most modem require a fixed speed of 19200 bps for phase C data
        transmission in class 2. Also class 1 defines a standard DCE-DTE
        bitrate of 19200 bps. Only class 2.0 is capable of handling bitrates
        higher than 19200 bps.

    DATABAUDRATE <DTE-DCE bitrate>
        Bitrate for initialisation of modem. Some older modem, especially those
        which are not capable of high speed data communication, do require a
        baudrate of 2400 bps.

    DIALWAIT <seconds>
        Time to wait between two dial tries.

    DIALRETRY <count>
        Number of dial tries. Default is '0'. That means after an unsuccessful
        call, fsend will terminate. If 'DIALRETRY' is defined, Fsend will try
        to establish a connection for the determined number of times until
        terminating.

    COVERPAGE <YES or NO>
        If set to YES a cover page containing several informations (e.g. your
        name, voice and fax phone number, name and fax number of the receiver,
        a short comment and so on) will be created as first fax page. Also see
        '-d' and '-m' command line parameters.

    COVERGRAPHIC <Bitmap file name>
        The named bitmap is placed in front of the cover page. Only black and
        white bitmaps (bitcount is 1 and planes is 1) can be used. Bitmaps
        smaller than a faxpage (1728 pixels) are centered, larger bitmpas are
        right truncated. If a covergraphic is defined, Fsend automatically
        uses fine resolution for the coverpage. The resolution of following
        pages depends on the filetyp and the usage of NOEOM (or '-NoEOM'):

        Pages produced from plain text are of normal resolution (204 x 98 dpi),
        bitmaps from a BMP are of fine resolution (204 x 196 dpi) and fax pages
        based on TIF are from a resolution as neer as the original (normally
        fine resolution). If 'NOEOM' is enabled, all pages follow the
        resolution of the coverpage.

    COMPORT <serial port>
        This keyword is mandatory. Even if Fsend is called using a port handle
        (from Frec) this keyword must exist! The name of the device is used to
        create a unique identifier for internal use!

    INITFIFO
		If a hardware fifo (UART 16550) is detected by COM-device driver, the
		fifo is initiallized to Rx=8 and Tx=16.

	CAPABILITIES <vr,br,wd,ln,df,ec,bf,st[,jp]>
        Default is 1,3,0,2,0,0,0,0,0 which means: high resolution, maximal
        9600 bps in V.29 modulation, 8 inches paperwidth, endless paperlength,
        1-D Huffman coded data, no ECM, no BFT and 0 ms wait between scanlines.

        With these values, successful transmission to each receiving station is
        possible. If the receiver is not capable of any of these values, Fsend
        will adjust to such values, the receiver can (and must) handle.

        vr (vertical resolution):
            00 . . . normal 204x98  dpi (R8 x  3.85/mm),
            01 . . . fine   204x196 dpi (R8 x   7.7/mm),
            02 . . . high   204x392 dpi (R8 x  15.4/mm),
            04 . . . extra  408x392 dpi (R16 x 15.4/mm),
            08 . . . 200x100 dpi,
            10 . . . 200x200 dpi,
            20 . . . 200x400 dpi,
            40 . . . 300x300 dpi,
            80 . . . 400x400 dpi (not defined in T.32)
        All values for 'vr' are in hexadecimal notation!
        Not all resolutions are supported!

        br (bit rate):
            0 . . .  2400 bps
            1 . . .  4800 bps
            2 . . .  7200 bps
            3 . . .  9600 bps
            4 . . . 12000 bps
            5 . . . 14400 bps

        wd (page width):
                    R8    R16   200   300   400
                    d/mm  d/mm  dpi   dpi   dpi
            0 . . . 1728  3456  1728  2592  3456 (A4 width)
            1 . . . 2048  4096  2048             (B4 width)
            2 . . . 2432  4864  2432             (A3 width)
            3 . . . 1216  2432                   (A5 width)
            4 . . .  864  1728                   (A6 width)
            Not all resolutions are supported!

        ln (page length):
            0 . . . A4 length, 297 mm (not supported)
            1 . . . B4 length, 364 mm (not supported)
            2 . . . Unlimited length

        df (compression scheme):
            0 . . . 1-D Modified Huffman (ITU T.4),
            1 . . . 2-D Modified read (ITU T.4),
            2 . . . 2-D Uncompressed mode (ITU T.4), (not supported)
            3 . . . 2-D Modified modified read (ITU T.6)

        ec (error correction):
            0 . . . do not use ECM
            1 . . . Enable Annex A/T.30, ECM (only supported in class 1)
            2 . . . Enable Annex C/T.30, half duplex (not supported)
            3 . . . Enable Annex C/T.30, full duplex (not supported)

        bf (binary file):
            00  . . Disable file transfer modes,
            01  . . Select enable BFT (ITU T.434), (not supported)
            02  . . Select document transfer mode, (not supported)
            04  . . Select edifact mode, (not supported)
            08  . . Select basic transfer mode, (not supported)
            10  . . Select character mode Annex D/T.4, (not supported)
            20  . . Selcet mixed mode Annex E/T.4, (not supported)
            40  . . Select processable mode (ITU T.505) (not supported)
        All values for 'bf' are in hexadecimal notation !!!

        st (time/scanline):
                    vr = 0    vr > 0
            0 . . .  0 ms      0 ms
            1 . . .  5 ms      5 ms
            2 . . . 10 ms      5 ms
            3 . . . 10 ms     10 ms
            4 . . . 20 ms     10 ms
            5 . . . 20 ms     20 ms
            6 . . . 40 ms     20 ms
            7 . . . 40 ms     40 ms

        jp (JPEG coding):
            00  . . Disable JPEG coding,
            01  . . Enable JPEG coding (ITU T.81), (not supported)
            02  . . Full color mode, (not supported)
            04  . . Enable preferred Huffman tables, (not supported)
            08  . . 12 bits/pel/component, (not supported)
            10  . . No subsampling (1:1:1), (not supported)
            20  . . Custom illuminant, (not supported)
            40  . . Custom gamut range (not supported)
        All values for 'jp' are in hexadecimal notation !!!

    NOECMDUMMY
        This keyword suppresses the generation of a (first) dummy HDLC frame.
        This dummy frame is sent to receiver if (a least) the first HDLC frame
        is twice rejected. The reason why that is so still is unknown, but it
        seems, that some fax modem does not send a frame limiting character
        (HDLC-flag) in front of first frame.
        Obviously, not all fax machine accept such a dummy frame, so you must
        disable it with this keyword.

    NEXTPAGE <text>
        If the footer line feature is not disabled, Fsend will create an
        information at the bottom of each line saying if there is an other
        page following the current one or if it was the last. The default
        text says "NEXT PAGE FOLLOWS" but it might be exchanged by any other
        text using 'NEXTPAGE'.

    LASTPAGE <text>
        Same as 'NEXTPAGE' but this text will be created if the current page
        was the last one. The default text says "END OF FAX PROCEDURE".

    DEBUGIDLEPRIORITY <value> or DEBUGREGULARPRIORITY <value>
        These keywords, which are mutual exclusive, define the priority (0-31)
        for the task (thread) which writes the data to FAXDEBUG file. Default
        is IDLEPRIORITY 30. Change this setting only, if you are absolutly sure
        knowing what you do! Lower priority may yield in a endless blocking
        debug_thread! No data will be written to FAXDEBUG and FSEND may become
        'uncloseable'. On very slow or high stressed machines, you can
        try REGULARPRIORITY 0, if IDLEPRIORITY blocks writing to FAXDEBUG.

    LOADIDLEPRIORITY <value> or LOADREGULARPRIORITY <value>
        These keywords, which are mutual exclusive, define the priority (0-31)
        for the task (thread) which reads in text or bitmaps and converts it
        to a fax pixel image while fax date is transmitted. Default is
        IDLEPRIORITY 31. Lower priority may slow down reading, yielding in
        no correct faxtransmission! LOADPRIORITY must be higher than
        DEBUGPRIORITY. On slow or high stressed machines, try
        REGULARPRIORITY 1. You can disable this priority switching by using
        the '-fastload' commandline switch (which is in fact the same as
        REGULARPRIORITY 0).

    LINESPACE <n>
        Same as ~LINE= in a text file but global. The generation of HEADER and
        FOOTER is not affected of this parameter. Default is '0' which means
        leading is 20% of font height.

    LOADFONT <x:\path\faxfont.FFF>
        You can load a prebuild (with FONTEDIT.EXE, supplied with the package)
        fax font for using in conversion of text files. Each 'handbuild' font
        has a font name (defined by you when saving the fontdata in FONTEDIT)
        which is a key to this font. This is a well tested, but quick and dirty
        feature of FSEND. Use it right or forget it. An other possibility, to
        construct fonts, is FAXVIEW, see also FAXVIEW.DOC!

    TEXTFONT <fontname>
        Default the font '16x16_standard', which is hardcoded in FSEND, is
        used to generate pixelimage from text files. With this keyword, you
        can define an alternate, but formerly preloaded with LOADFONT, fax
        font. This font is used if no '~FONT=<fontname>' directive is placed
        in a text file and in the informational part of COVERPAGE.

        Note: fontname is the NAME of the font (as you define when saving
        font data in FONTEDIT) and is NOT the name of the fontfile used in
        LOADFONT!

        Inline directives, which MUST start at the beginning of a new line,
        for text files:

            ~FONT=<fontname>
                Select a preloaded (LOADFONT) fax font. Use here the NAME
                of the font you have given when saving fontdata in FONTEDIT
                and not the name of the fontfile! At the start of each new
                text file, 'fontname' is resetted to TEXTFONT.

            ~IMAGE=<filename.BMP>
                Defines a black and white bitmap to be inserted at that
                position into the pixel image of the text file. Bitmaps
                smaller than the fax page, will be centered. Larger bitmaps
                will be right truncated. Fax pages from text files will be
                generated in normal resolution (204 x 98 dpi). Therefor,
                the bitmap (which is normaly in a symetrically resolution)
                is vertically reduced in resolution (not shrinked). Two
                consecutiv pixel lines are 'ored' together to form the new
                pixelline. In further versions of Fsend, resolution of text
                pages may be defineable.

            ~LEFT=<mm>
                Default 8 mm border on left side of page is used. You can
                define any other suitable value. Once altered, left margin
                is constant for the whole fax text document and is affected
                only by a new ~LEFT statement.

            ~RIGHT=<mm>
                Default 8 mm border on right side of page is used. You can
                define any other suitable value. Once altered, right margin
                is constant for the whole fax text document and is affected
                only by a new ~RIGHT statement.

            ~LINE=<mm>
                The default value of '0' yields in a interline spacing of
                aproximately 20 % of fonthight. You can chose any value
                between 0 and 270. The special value -1 disables interline
                spacing and is so preferable when blockgraphic should be
                converted. See also LINESPACE above.

    INFOFONT <font name>
        Default the font '8x8_standard', which is hardcoded in FSEND, is used
        to generate pixelimage for HEADER, FOOTER, NEXTPAGE and LASTPAGE.
        With this keyword, you can define an alternate, but formerly preloaded
        with LOADFONT, faxfont.

        Attention: The hardcoded font has some special characters in it, if
        building a new font, DO NOT alter this characters from 8x8_standard.

        Note: font name is the name of the font (as you define when saving
        fontdata in FONTEDIT) and is not the name of the fontfile used in
        LOADFONT!

    LOGLEVEL <n>
        Writing to log file (also see 'FAXDEBUG' keyword) depends on this
        value (0 to 5):
            0 . . do NOT write to FAXDEBUG (is equal to 'FAXDEBUG NUL')
            1 . . ERROR only
            2 . . ERROR + SEND + RECEIVE only
            3 . . ERROR + SEND + RECEIVE + ACTION only
            4 . . ERROR + SEND + RECEIVE + ACTION + WAIT FOR only
            5 . . ERROR + SEND + RECEIVE + ACTION + WAIT FOR + INFO (default)

    DEBUG
        Enables a lot of stuff for debugging. Do not use, because LOG will
        increase enormous.

    FRECCFG <configfile> [commandline switches for FREC]
        The full name and path to Frec configuration file. If defined, Fsend
        may be used as a frontend to act as pollserver and faxreceiver. In
        fact the same as Frec in conjunction with Fsend.

        If (optional) commandline switches are defined, the call to FREC is
        performed like:

        FREC -c<configfile> -k<outcompression> -p<comhandle> [-task<n>]
            -sWAIT_OK <commandline switches for FREC>

        If TaskNo is defined, it is also submitted.

        It is no longer supported, to choose between FREC.EXE and FREC.DLL!
        From now on, FSEND searches for FREC.DLL in LIBPATH and if not found,
        FREC.EXE is called.

    NOATD
        Switch to suppress 'ATD' in class 1 if an EOM situation occures and
        modem is not able to handle ATD in class 1 correct. Try also 'NOEOM'
        keyword to workaround modem misbehaviour.

    MINPAGELENGTH
        Can be used, to determine the minimal length of fax page. Default is
        3 cm, because a lot of fax machines and fax modem will reject shorter
        pages (by RTN). Note: The maximum valid value is 30 cm.

	INBOUND <path to inbound>
        If DESTNAME and DESTADDR are also defined, a netmail (????????.PKT)
        is created each time a fax is transmitted.

    DESTNAME <string>
        If this, INBOUND and DESTADDR is defined in FSEND.CFG, a netmail
        is created and addressed to.

    DESTADDR <FidoNet style address>
        Must be defined to create announcing netmail.

    SRCNAME <string>
        Used to form the 'From:' part of the announcing netmail.
        Default is: "FSEND".

    SRCADDR <FidoNet style address>
        Normally this is the address of local system. Defaults to DESTADDR.

	SUBJECTSENDFAX <string or %>
        Used in creation of announcing netmail on transmitting fax. If '%' is
        the first (or only) character, the filename from which the fax is sent
        will be placed in subject part of netmail.
        Default is: "Announcement of outgoing FAX".

	FLAGDIR <path>
		Path, were a semaphor file is created if used in conjunction with
		the -FaxLog feature and a redial is neccessary.

	EXITSEM <semaphor name>
		Semaphor file to force mailer (BinkleyTerm or Cantaloup) to exit with
		error level. Should be either BTEXIT (for Binkley) or CLEXIT (for
		Cantaloup).
		In combination with TASK and ExitErrorLevel a semaphor file is created.

	EXITERRORLEVEL <level>
		Errorlevel for mailer when forced to exit by semaphor.


    Additional information:

    All file and path specifiers in configuration file are checked against
    %<environment>%. If a valid environment entry is found, %<env>% is
    replaced by the content of the variable, e.g.:

        SET LOG=D:\LOGFILES

        BinkLog %LOG%\BINKLEY%TASK%.LOG
        FaxDebug %LOG%\FREC%TASK%.LOG

    A special 'replacement' is done in all file name entries in configuration
    file when '%TASK%' is detected. %TASK% (must be uppercase) is replaced
    by the defined task number.

    If a debug file is defined and this debug file can not be accessed, than
    a 'default' in the root of the current drive (\FSEND.DEB) is used instead.

    It is strongly recommended to use a debug file! In case of misbehaviour
    99% of faults can be localized quickly and (from the author :-).



-------------------------------------------------------------------------------
    COMMAND LINE PARAMETERS AND SYNTAX
-------------------------------------------------------------------------------

    The format of the commandline is as follows:

    FSEND <switch> <switch> ...

    Each argument must immediatly follow the switch (no blanks). Some switches
    allow entries which have blanks, eg. to form names or comments.

    -ForceV33
        If receiver signals bit rates higher than 9600 bps always use V.33
        (class 1 only).

    -ForceV17
        If receiver signals bitrates higher than 4800 (and even if V.17 is
        not signaled) use V.17 (class 1 only).

    -SendPWD<numerical_password>
        Is used to create a PWD (PassWorD) frame for an outgoing fax. This
        must be used if destination has password protection for incoming fax.
        Attention: Only '0' - '9', '#' and '*' are valid characters! All other
        characters are invalid and strictly discarded by Fsend. String length
        is limited to 20 characters. '-SendPWD' can be used in Class 1 and 2.0
        (if supported by the modem) only!

    -SendSUB<numerical_subaddress>
        Is used to create a SUB (SUBaddress) frame for an outgoing fax. This
        can be used, to send to a special address in receiver's domain (if
        supported by receiver).
        Attention: Only '0' - '9', '#' and '*' are valid characters. All other
        characters are invalid and strictly discarded by Fsend. String length
        is limited to 20 characters. '-SendSUB' can be used in Class 1 and 2.0
        (if supported by the modem) only!

        See also '-g' commandline switch to define phonenumber.

    -FaxLog
        This parameter enables a special mode of operation. For proper
        operation of this feature 'FAXLOG', 'FAXIDX' and 'FAXPATH' have
        to be defined correctly. Fsend will send a fax that is created
        by other applications fax printer driver.

        If Fsend is called with '-task<n> -c<file name> -FaxLog' parameters
        it will extract all required information from FAXLOG and
        start sending the fax if the given date and time entry is empty or
        either equal or less actual date and time.
        Note: Also see new errorlevel values!

        To create a fax throug other applications fax printer driver you
        have to act as follows:

        An application (or simply 'COPY CON LPTx', where x is the printer
        port assigned to special printer driver) must print to
        fax printer driver. If the data send to the printer driver is not
        plain ASCII text you have to create a 'FAX.CGS' file which contains
        all information required to create the fax. If the data send to the
        printer driver is plain ASCII, this data also can be placed at the
        very beginning of the text file. Following lines are required:

            >>TO=<name of receiver>,*,<fax no of receiver>
            >>AT=<time to send>,<date to send>

        The first line will make the fax printer driver creating the fax. A
        FAXLOG entry like '<idx no>,,,1,Spool ,,1,0,99,,<name of
        receiver>,,<fax no of receiver>,,,,,,,,,' will be created.
        The second line is optional. If used the fax will not be sent until
        date and time arrived. Using both lines the printer driver will
        create a log entry like '<idx no>,23-Jan-97,14:32,1,Spool ,,1,0,99,,
        <name of receiver>,,<fax no of receiver>,,,,,,,,,'.

        The date must be strictly entered in the format DD-MON-JJ, where
        MON is the english abbreviation for the month with first character
        uppercase. Day of month must contain leading zero if below 10!

        Optionally, a third line containing a short 'comment' (for cover
        sheet) can be added:

            >>INFO=<comment>,*,*,*

        Maybe, in further versions, a simple textmode utility will be
        supplied, to create (and maintain) FAXLOG file for the
        above use ...

    -Quiet
        Fsend is switched to an absolutly quiet mode of operation. Only
        log file is written and very short messages to stderr at the begin
        and end of operation. You can redirect output of stderr to a file
        by using '2>>error.log' which yields in:

            + 14 Mar 11:50:41 FSEND Begin, v1.23b
              14 Mar 11:50:46 FSEND HangUp <hangup_code>
            - 14 Mar 11:50:46 FSEND End. [<errorlevel>]

    -Task<n>
        Where <n> specifies the task number to be used. See also [TASK <n>]
        and [COMMON] keywords in configuration file. If this parameter is
        not used the common task will be used.

    -c<config file>
        Default Fsend assumes the configuration file is named FSEND.CFG and
        located in the current directory. The '-c' command line parameter
        can be used to define an other path and file name.

        Configuration file can also be supplied via environment:

        SET FAX=x:\path\fsend.cfg

        or

        SET FAXCFG=x:\path\fsend.cfg

    -o<file name> [<page indicator>]
        Input file for fax transmission. You can send black and white
        bitmaps from type .BMP or .TIF or text files (see 'TEXTEXTENSION'
        keyword). More that one '-o' parameter is allowed in a single
        command line. Wildcards (*, ?) also are allowed. A blank separated
        'page indicator', following the file name is possible. For more
        information on that see '-o@' command line parameter.
        Note: The 'page indicator' must be one number (only digits,
        no blanks) and should have not more than 20 digits.

    -o@<file name>
        As an enhancement to the '-o' option, you can define a pointer
        file, which contains all the file names instead. Each line must
        contain only one file name. Wildcards are allowed. In accordance
        to 'selective poll' a 'page indicator' may also be used:

        Content of such a pointer file:

            X:\PATH\NEWLIST.TXT
            Y:\OTHERPATH\FILELIST.TXT 1
            Z:\NEWPATH\ECHOLIST.TXT 2

        Which means, NEWLIST will be sent to everybode whereas FILELIST only
        will be sent if remote station is supplying '1' in SEP frame and
        ECHOLIST only will be sent if '2' is supplied in SEP frame. If the
        remote station does not use any SEP frame, than ALL three files will
        be sent.

    -g<phone number>
        Enter the number of the fax you want to send to. The number is
        transmitted as it is to the modems dial command. So special dial
        modifiers may be included here.

        Alternativly to the '-PollSUB' a 'subaddres' in receivers domain may
        also here specified by appending a "'" and the (numerical) subaddress:

        "-g0043 1 701 99" or "-g47110815" or "-g0456789'123" are valid
        dial commands. Last one shows subaddressing to 123. Read also
        the definition of FAXPATH in FREC.DOC.

    -#<idx no>
        This is a special commandline option to easyly send fax files
        created by other applications. Simpley enter the index number of the
        fax file to be sent (e.g. for FX000123.FAX you have the enter
        '-#123'). If you want to send the fax file which is created last,
        enter '-#?' and the idx number will be generated using information
        in FAX.IDX file. If 'NOLOGONBAD' is not defined, an entry in
        FAX.LOG is done.

    -d<name> or
    -TO:<name>
        You can define here the name of the receiver of the fax file, e.g.
        '-dMr. John Smith'. Do not use any special characters the operating
        system interprets for own use, or use the '"' character to embed, like
        '"-dMr. & Mrs. Hoover"'.

    -r<name> or
    -FROM:<name>

	    You can define here a 'LocalName' which will overwrite the name
        supplied in CFG. See '-d' for some restrictions.

    -m<comment>
        Like in '-d' option, you can enter a SHORT message to the receiver,
        which is print in the coverpage. Sample: '-mLast news from our
        meeting'.  This option implies, that '-o' can be omitted. Short
        fax messages without generation of a text file are possible, only
        a coverpage (must be defined in configuration file) is sent.

    -NoCover
        A simple 'shortcut' to suppress generation of coverpage if defined
        in configuration file.

    -NoEOM
        Commandline switch to suppress EOMs in multidocument fax. See NOEOM
        keyword in configuration file.

    -x
        Each fax page is stored in a bitmap (FXDTnnnn.BMP) in the same form
        as it is transmitted. The 'nnnn' is a number from 0001 to the page
        count. This parameter is useful for verifying the generation of
        cover page and text files.

    -h or -?
       A short help screen is shown. This printout can not be redirected into
       a file, because VIO functions are used!

    -v<faxviewer>
	    An external fax viewer (please refer FAXVIEW.DOC for more information)
	    can be used to display an outgoing fax in realtime on the screen.

	    There are TWO possible modes to use:

    	1) <faxviewer> is the name of a compatible viewer (obviously
	    	FAXVIEW.EXE), which will be started (by DosStartSession) and closed
		    by FSEND (by WM_QUIT).

    	2) <faxviewer> is the name of a pipe (eg. '\PIPE\LINE1'). In this case
	    	the viewer (FAXVIEW.EXE) must be already loaded (see FAXVIEW.DOC)
		    and is only actived by FSEND (by pipe).

    -BITS or -LARGE or -STANDARD or -PREVIEW
	    Scaling option for optional external fax viewer.
	    Note: Do not use 'scaled' option in FAXVIEW.EXE.

    -p<com port handle>
        If this parameter is used, FSEND assumes it is called by any other
        application or other front end.
        Note: The port handle is not the same as the port number (e.g. COM1)!
        All initialisation must be done by calling front end.

-------------------------------------------------------------------------------
    Assumptions of WORKING CONDITIONS:
-------------------------------------------------------------------------------

    There are some dedicated working conditions for FSEND, depending on what
    job it shall do. FSEND recognizes these condition by interpreting its
    commandline switches:

    -P<porthandle>  -FDIS/-FDTC  -G<phoneno>  -FaxLog  CONDITION  Use
    ---------------------------------------------------------------------
        NO              NO          NO          NO          (1)     FE
        NO              NO          NO          YES         (2)     S
        NO              NO          YES         NO          (3)     S
        NO              NO          YES         YES         (4)     !
        NO              YES         NO          NO          (5)     !
        NO              YES         NO          YES         (5)     !
        NO              YES         YES         NO          (5)     !
        NO              YES         YES         YES         (4)     !
        YES             NO          NO          NO          (6)     PS
        YES             NO          NO          YES         (7)     S
        YES             NO          YES         NO          (8)     S
        YES             NO          YES         YES         (4)     !
        YES             YES or -B   NO          NO          (9)     PS,S,NoInit
        YES             YES         NO          YES        (10)     !
        YES             YES         YES         NO         (10)     !
        YES             YES         YES         YES         (4)     !

    FE ..... Frontend
    PS ..... PollServer
    S ...... FaxSender
    NoInit . CFGs 'Init' not used
    ! ...... irregular condition


    1)  Standalone frontend. FSEND can act as a sender/pollserver or receiver
    (by calling FREC). At least one file (-o) must be specified or coverpage
    must be enabled AND a message (-m) must be supplied. If no filename or no
    coverpage is enabled, FSEND stops with error, else FSEND waits for a caller

    2)  Standalone fax sender. All information for this job is excerpted from
    FAXLOG. if no fax with status 'Spool' or no phonenumber in FAXLOG, FSEND
    stops with error, else FSEND starts to send.

    3)  Standalone fax sender. At least one file (-o) must be specified or
    coverpage must be enabled AND a message (-m) must be supplied. If no
    filename or no coverpage is enabled, FSEND stops with error, else FSEND
    starts to send by calling the supplied phonenumber.

    4)  Irregular combination. Phonenumber is TWICE defined (by -g and in
    FAXLOG). FSEND stops with error.

    5)  Irregular combination. -FDIS or -FDTC is defined, but no porthandle
    is supplied by -p. FSEND stops with error.

    6)  Fax pollserver called with a porthandle from any other application
    which has allready opened the com port (and initialized). At least one
    file (-o) must be defined or coverpage must be enabled AND a message (-m)
    must be supplied. If no filename or no coverpage is enabled, FSEND stops
    with error, else FSEND waits for a caller.

    7)  Fax sender called with porthandle from any other application which has
    allready opened the com port (and initialized). All information for this
    job is excerpted from FAXLOG. If no fax with status 'Spool' or no
    phonenumber in FAXLOG, FSEND stops with error, else FSEND starts to send.

    8)  Fax sender called with porthandle from any other application which has
    allready opened the com port (and initialized). At least one file (-o)
    must be specified or coverpage must be enabled AND a message (-m) must be
    supplied. If no filename or no coverpage is enabled, FSEND stops with
    error, else FSEND starts to send by calling the supplied phonenumber.

    9)  Fax pollserver called with a porthandle from any other application
    which has allready opened the com port (and initialized) and has allready
    an active fax connection in or prior to PHASE B. At least one file (-o)
    must be specified or coverpage must be enabled AND a message (-m) must be
    supplied. If no filename or no coverpage is enabled, FSEND stops with
    error, else FSEND immediatly enters PHASE B of a transmitting station,
    assuming the supplied values for DIS or DTC. If not used in Class 1, -b
    commandline switch may be supplied instead of DIS/DTC. Due to the fact,
    that there is no difference for FSEND if satisfying a poll or simply does
    a send job, this condition can also be used by any other application to
    make a normal send (other application must allready have dialed/answered
    and have a fax connect).

    This is the normal situation, when FREC detects a caller who want to poll
    a fax and routes the call to FSEND to satisfy poll.

    10) Irregular combination. DIS or DTC supplied (in fact an active
    connection) and phonenumber (from commandline or FAXLOG) is also
    supplied.

-------------------------------------------------------------------------------
    ERROR LEVELS USED BY FSEND:
-------------------------------------------------------------------------------

    0 . . . all sendjobs (in accordance to standard) done.
    1 . . . wrong commandline switch
    2 . . . phonenumber AND called with FDTC/FDIS OR no files to send
    3 . . . no or wrong configuration file
    4 . . . Nothing to do in FAX.LOG (no 'Spool' entries)
    5 . . . Too less information in or no FAX.LOG
    6 . . . Spool active, but delayed
    10  . . Invalid comport or used from other application
    11  . . No Connect after dial (can be BUSY, NO CARRIER, NO ANSWER etc.)
    12  . . Error (user ESC) after dial
    20  . . DATA connect in frontend mode, session still active
    100 . . DebugThreadError
    101 . . BitmapThreadError
    102 . . CompressionThreadError
    103 . . ComInThreadError
    104 . . TimeThreadError
    200 . . send maybe correct, but nonstandard termination
    251 . . Error after connection
    253 . . ModemError
	254 . . ComPortError
	255 . . Serious problem, can be anything, use '2>error.log' to localize




-------------------------------------------------------------------------------
	HISTORY
-------------------------------------------------------------------------------

	Version 1.34:
		Large parts of code (esp threadhandling, memoryallocation, exception-
	handling and CFG/CMD-handling) was redesigned. All parts of code, which are
	also in FREC and ANSW were put to FAXPROC, which is from now on a dynamic
	link library (FAXPROC.DLL). Linking of C-runtime is never more statically,
	instead, C-runtime is linked dynamically (at loadtime) for FSEND, FAXPROC
	and IMGPROC. So, the overall amount of codesize was reduced. Some keywords
	in CFG were also altered:

		INBOUNDSEND    -->    INBOUND (sorry for twice altering)
		SUBJECTSEND    -->    SUBJECTSENDFAX
	NEW:
		InitFifo (see above)

    Not longer supported:
        FRECDLL (see FRECCFG)

	Finally, the COM port open methode is now checked in FAXPROC. Only if COM
	is opend in READWRITE and SHARE_DENYREADWRITE, work is continued! I hope
	some problems (when called from a mailer, which uses a patched MAXCOMM to
	open COM in SHARE_DENYNONE mode) are solved now. Also SIO.SYS in
	'share mode' should never more work!

	Maybe some users will disagree, but 'sharing' a communication port is NOT
	usefull on a multitasking environment! Each application MUST have unique
	access to its own resources.

	Version 1.33:
		Only internal test version and not distributed.

	Version 1.32:
	Serious bug in XON/XOFF handling caused an infinit loop (and 100% CPU used).
		In combining TIF procedures in IMGPROC.DLL, check for validy of
		PhotometricInterpretation was lost. Is fixed also now.

	Version 1.31:
		FSENDs commandline switches are partly changed to have same
		meaning as in FREC:
			old     	new
			'-i' 	=> 	'-o'
			'-f' 	=> 	'-l' (undocumented)
        	'-w' 	=> 	'-p'
        	'-FROM' => 	'-r'
        	'-r'	=>  sending of raw data file is not more supported!

        Like FREC, FSEND can from now on also 'show' a picture of the outgoing
        faxpage by using FAXVIEW.

        Due to enhancements in FREC, FAXPATH must be (once) defined and is
        used to form fully qualified drive, path and filename for FAXIDX and
        FAXLOG. Both FAXLOG and FAXIDX have defaults (FAX.LOG and FAX.IDX)
        and should only be (re)defined if other than default. As FREC can
        accept more than one FAXPATH, FSEND will use (if same CFG for both
        is supplied) only the FIRST found entry!


    Version 1.30:
        some new keywords (read above) and parts of T.32 are implemented.
        Also higher resolutions like in T.30 defined will be supported
        (untested)!

    Version 1.29:
        from now on, FSEND and FREC can use one and the same configuration
        file. Certain keywords were updated, like:
			INBOUND -> INBOUNDSEND and INBOUNDREC
            SUBJECT -> SUBJECTSEND and SUBJECTREC
        It is recommanded, to distinguish between Frec and Fsend portions
        of configuration file by '[TASK <n>]' keyword.

    Version 1.28:
        a serious and hard to find BUG in FSEND was eliminated. This BUG was
        only active if SOURCE was 2-D Read (G4) TIF AND faxtransmission was
        2-D Read AND first transmitted page was THIS 2-D Read TIF.

        Many THANKS to Massimo Fantin from Italy, who has 'needled' me to
        find this bug (some code for IMGPROC was still also in FSEND and was
        only called if source AND transmission was in 2-D)

        TIFPROC.DLL now is named IMGPROC.DLL, because in WARP 4.0 MMOS2 is a
        new DLL named TIFPROC.DLL!

    Version 1.27
        is build with MINOR changes from version 1.25a. TIFPROC.DLL is
        reduced because LZW (Lempel, Ziv & Welch) compression is under
        patent regulation in some countries. So TIFPROC is no longer able
        to handle Compression=5 (normally known as LZW). TIFPROC is 'under
        study' and will be changed/upgraded when LZ-compression will work
        in unrestricted manner!

    Versions 1.25 and 1.26
        were ALL REJECTED! To much problems arised with TIFPROC.DLL!

    Version 1.26
        is released, because 1.25 was WRONG (do NOT use it) ....




-------------------------------------------------------------------------------
    FINALY:
-------------------------------------------------------------------------------

    Please also read carefully the sample configuration file.

    FSEND and FREC are updated either if there is a serious bug or if some
    new or requested features were added. The documentation is updated, if
    there is time in the authors 36 hour day :-).

    Please fell free to contact the autor:
        FidoNet 2:310/14.59
        Internet Harald.Pollack@OMV.CO.AT

    Many thanks to Bernhard Seidl and Gerold Pummer for excessive tests
    of various (beta) versions of Fsend.

    And last, but not least, my greatest thanks to WOLFGANG HOFFMANN,
    who was in fact the one who believes in this program and who gave me
    all the necessary standards to do things in the right way.


<end of doc>