ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  MAXterm á2.01
  The Original MAX Graphics Compatible Terminal Program
  Copyright 1995-Current * Larry L. Athey * BBS Utiliteez Software
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  System Requirements:
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  IBM or compatible PC with a 386 or better (Preferably Better) CPU. MAXterm
  has been tested on as small as a 386/SX40 and as high as a Pentium 133. If
  you are running a 386, you can expect MAXterm to run a little slow, sorry.

  DOS 3.0 or greater, no special operating system required. This program will
  also run perfectly in a DOS session under MS Windows or OS/2 as well...This
  program should never be used under DesqView...

  400K (or greater) free conventional memory.

  1 Meg (or greater) free XMS or EMS memory.

  SoundBlaster compatible digital sound card. (Optional)

  Microsoft compatible mouse...This is a MUST!!!

  SVGA video card with at least 1 Meg of video RAM. If your video chipset on
  your video card is not directly supported by this program, you will need to
  make sure your video card is at least VESA compatible. If your video card
  does not have an on board VESA BIOS, you will need to load the VESA driver
  TSR that came with your computer or video card before running this program.
  Keep in mind that running MAXterm in generic VESA mode will result in slow
  performance.

  Configuring your video card's chipset is done through the MAXVIDEO.CFG file,
  which is a plain text file with the video chipset ID number on the first
  line of the file. Below is a list of the supported chipsets and their ID
  numbers:

  ID - Video Chipset Brand/Series
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  0  - Attempt To Auto Detect Chipset
  1  - Generic VESA Support
  2  - Ahead A series
  3  - Ahead B series
  4  - ATI 18800
  5  - ATI 18800-1
  6  - ATI 28800/38800/68800/88800
  7  - Chips & Technologies 82c451/455/456
  8  - Chips & Technologies 82c452
  9  - Chips & Technologies 82c453
  10 - Genoa 6000 series
  11 - Oak OTI-067
  12 - Paradise PVGA1a
  13 - Paradise WD90C00/WD90C10
  14 - Paradise WD90C11/30/31/33
  15 - Trident 8800 series
  16 - Trident 8900/9000 series
  17 - Tseng ET3000 series
  18 - Tseng ET4000 series
  19 - Video7
  20 - Cirrus Logic 5400 series
  21 - S3
  22 - NCR 77C22/77C32
  23 - Oak OTI-077
  24 - Oak OTI-087
  25 - Type 25 (Reserved)
  26 - Cirrus Logic 6400 series
  27 - Advance Logic 2000 series

  If you select ID #0 and get nothing but garbage when you fire up MAXterm,
  this usually means that MAXterm could not detect your video chipset, nor
  could it auto detect VESA compatibility either. If you have also tried to
  load a VESA driver TSR in advance and are still having no luck, you will
  need to force VESA support ON by placing a number 1 on the first line of
  the MAXVIDEO.CFG file. If this still doesn't work, it is obvious that the
  MAXterm program will not work with your video card. In this event, please
  send me the specifications on your video card so I can see if there is a
  chance that direct support can be added for it.

  You will need to have shareware or registered copies of ARJ, LHA, PKWARE,
  and RAR archivers on your system located in your "Archiver Path" in MAXterm.
  If you don't have any of these, you will need to get them before you can
  run this program. If these utilities do not exist in your Archiver Path you
  will not be able to unpack or re-package graphics resource packages.

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  Installation:
  ÄÄÄÄÄÄÄÄÄÄÄÄÄ
  Before this program can continue installing, you will need to know a few
  things about your system in advance. First of all, the default archiving
  method used by MAX products is PKZIP, you will need to know the path to
  PKZIP.EXE and PKUNZIP.EXE ahead of time. If these already exist in your
  DOS path, the installation program will automatically find them for you.

  You will also need to know the comport number and IRQ that your modem is
  attached to. This program will default to UART communications as well as
  to a 38400 baud locked port speed. You can change these settings to suit
  your system as needed.

  Lastly, if you have a "SoundBlaster" compatible sound card installed you
  will need to know the port hex address, IRQ, and DMA channel of the card
  as well. This information is usually available in your AUTOEXEC.BAT, or
  if you run MS Windows, check the "Control Panel" settings for your sound
  card to obtain this information.

  To continue, simply copy the contents of this archive to any directory of
  your choice. Run SETUP.EXE with no parameters and the program will do all
  of the work for you, and be sure to follow *ALL* on screen instructions!!

  Repeat this process when upgrading from a previous version of MAXterm....

  Installation Problems:
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  Major changes have been made from MAXterm v1.XX to MAXterm v2.XX, and the
  installation procedure is one of the major changes. A lot of sysops, web
  masters, and CD-ROM manufacturers process files with "Upload Processors"
  and there are quite a few of them that think it's wise to convert any and
  all internal archives to their favorite archive format. BZZZT!!!...NOT!!!
  This was causing problems with people trying to install MAXterm and then
  being blasted with messages saying that the program couldn't find any of
  the icon libraries because the person they got it from converted the file
  DEFAULT.PKG to DEFAULT.ZIP or some other archive format. MAXterm is fully
  dependent on the SETUP.EXE to install the program, and now file names and
  their CRC32 values are verified to prevent any possible tampering. So now
  you can rest assured that when you install MAXterm, you will always have
  an authentic installation archive. The only way to assure that SETUP.EXE
  is authentic is to get your MAXterm archive directly from the author, but
  hopefully people will find better things to do than to tamper with that..

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                 To Obtain An Authentic Copy Of This Program:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Contact: 1:14/703@FidoNet             Or: USA MAX Graphics HQ-BBS ³
     ³          411:1500/0@ivNET                 (308)762-2239           ³
     ³          121:101/2@AllianceNet            FAX or Data Calls       ³
     ³          maxgfx@juno.com                  ANSI/ASCII/MAX (No RIP) ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ