HamComm
                                  Version 2.3

                                February 5th 1994




                                W. F. Schroeder

                                    DL5YEC



















         HamComm 2.3                                 Table of Contents


                               Table of Contents


         1 Introduction  ........................................... 1
         2 Trial Use License ....................................... 1
         3 Exclusion of warranty ................................... 2
         4 System requirements ..................................... 2
         5 Installation  ........................................... 3
         6 Startup ................................................. 3
         7 Config file HC.CFG  ..................................... 4
         8 Screen layout ........................................... 4
         9 Help system ............................................. 5
         10 Interface schematics ................................... 5
         11 Receive circuit  ....................................... 5
         12 PTT circuit  ........................................... 6
         13 Transmit circuit ....................................... 6
         14 External converter ..................................... 7
         15 External AFSK  ......................................... 7
         16 Signal decoding  ....................................... 8
         17 Macro keys ............................................. 8
         18 Macro files  ........................................... 9
         19 SHIP/SYNOP decoder ..................................... 9
         20 Scope function ........................................ 12
         21 Spectrum function  .................................... 13
         22 Bitlength statistics .................................. 15
         23 Converter checkout .................................... 16
         24 Port address .......................................... 16
         25 Op-Amp power supply  .................................. 18
         26 IRQ number ............................................ 20
         27 Appendix A - Interface schematics  .................... 21
         28 Appendix B - Key assignment summary  .................. 22




















                                       i


         HamComm 2.3                Manual              February 5th 1994




         1.  Introduction

         HamComm  is  a program for ham radio communications.  Version
         2.2  supports  reception  and  transmission  of amateur radio
         teletype  and Morse code signals.  Weather station reports in
         the SHIP and SYNOP format can also be decoded.

         A  converter or modem chip is not required.  The audio output
         of  the  receiver  is  connected  to  the  serial port of any
         PC/XT/AT  compatible computer thru a very simple and low-cost
         circuit.  Only one IC is needed (Op-Amp LM741 or similar) and
         a  few  diodes, capacitors and resistors.  The supply current
         is  drawn  from  the serial port.  For transmission the audio
         signal  from  the  speaker or serial port is connected to the
         microphone  input  of  the  transmitter  thru  a  passive R/C
         filter.     Audio    frequency   generation   and   decoding,
         serial/parallel conversion and all other signal processing is
         done by the program.


         2.  Trial Use License

         HamComm 2.3 is NOT a public domain program.

         Copyright (c) 1990,1991,1992,1993 and 1994 by W. F. Schroeder.
         All rights reserved.

         You are hereby granted a limited license to use this software
         for  evaluation  purposes  for  a  period of 30 days.  If you
         intend  to  continue  using  this  software  after the 30 day
         evaluation  period,  you  must make a registration payment of
         $20 or DM30 to:

                     W. F. Schroeder
                     Augsburger Weg 63
                     D-33102 Paderborn
                     Germany


         Please  note:  the bank will charge up to $5 to cash a cheque
         from   a  foreign  country.   For  this  reason  please  send
         banknotes or add another $5 to your cheque.







                                     - 1 -


         HamComm 2.3                Manual              February 5th 1994




         3.  Exclusion of warranty

         The  author  provides  absolutely  no warranty, to the extent
         permitted  by  applicable  state  law.  Except when otherwise
         stated  in  writing,  the author and/or other parties provide
         this  program  "AS  IS"  without warranty of any kind, either
         expressed  or  implied,  including,  but  not limited to, the
         implied  warranties  of  merchantability  and  fitness  for a
         particular  purpose.   The  entire risk as to the quality and
         performance  of  the program is with you.  Should the program
         prove  defective,  you  assume  the  cost  of  all  necessary
         servicing, repair or correction.

         In no event unless required by applicable law will the author
         and/or  any  other  party  who may modify and/or redistribute
         this program be liable to you for damages, including any lost
         profits,   lost  monies,  or  other  special,  incidental  or
         consequential  damages arising out of the use or inability to
         use  (including but not limited to loss of data or data being
         rendered inaccurate or losses sustained by third parties or a
         failure  of  the  program to operate with any other programs)
         this   program,   even  if  you  have  been  advised  of  the
         possibility  of  such  damages, or for any claim by any other
         party.


         4.  System requirements

         HamComm 2.3  will  run  under  MS-DOS  3.x  or higher on any
         PC/XT/AT-compatible  computer  with  at  least  320KB of free
         memory.   A  harddisk is recommended.  Because of the size of
         the  program  file  there may be not enough space to copy all
         required  files onto a 720KB diskette.  On slow systems, e.g.
         8088  CPU, some functions may not work as expected or may not
         work at all.

         HamComm  will  automatically detect the type of video adapter
         in  use.  MDA, CGA, EGA, VGA and Hercules are supported.  The
         graphics  display  functions  are not available on MDAs since
         the  MDA  has  no graphics mode.  No attempt has been made to
         avoid screen flicker (snow) on cheap CGAs.

         HamComm  will probably not run under any kind of multitasking
         software  like Desqview, Windows, Windows NT or OS/2 since it
         needs  direct control of the interrupt controller, timer chip
         and serial I/O hardware.



                                     - 2 -


         HamComm 2.3                Manual              February 5th 1994


         5.  Installation

         For   installation   on   a  harddisk  you  should  create  a
         subdirectory  HAMCOMM  and  CD to that directory.  HamComm is
         distributed  as  a  .ZIP or .EXE file.  To unpack a .ZIP file
         you  need  a program like UNZIP or PKUNZIP.  The .EXE version
         is  a  'self-extracting  archive' that contains all the files
         and  a build-in unpack program.  In both cases the files will
         be created in the current directory.

         Please read the files README, HC.CFG and CHANGES !


         6.  Startup

         To  start  HamComm  type  HC at the DOS prompt and hit ENTER.
         The  interface circuit is not needed if you just want to play
         with the program.

         HamComm  normally uses the currently selected video mode.  If
         you  have  an EGA or VGA card with an EGA/VGA monitor you can
         also  switch to 43 or 50 lines.  Try option -L43 to switch to
         43  lines on EGA/VGA cards or -L50 for 50 lines on VGA cards.
         If  the  card  already  is in one of these modes, option -L25
         selects 25 lines.

         Many  SuperVGA  cards  have special text modes e.g.  80x60 or
         132x44.   Activate  the desired mode before starting HamComm.
         Most  cards come with a utility program to do this.  Only the
         modes  where  the video display buffer starts at segment B800
         are supported.

         HamComm  assumes  that  the original PC display character set
         known as "codepage 437" is active.

         On  startup the program identifies the video card and monitor
         in  use  and  automatically  selects  the  graphics  mode for
         highest   resolution.    Some  program  functions  require  a
         graphics   mode   for  display  of  the  input  signal.   The
         identification  may  fail  because of compatibility problems.
         By selecting one of the following commandline options HamComm
         can be forced to use the specified mode:

                 Option  Mode      Resolution

                  -cga    6        640x200  2-color
                  -ega   10h       640x350 16-color
                  -vga   12h       640x480 16-color
                  -herc  Hercules  720x348  2-color


                                     - 3 -


         HamComm 2.3                Manual              February 5th 1994


         If  you  have  a computer with LCD display and readability is
         poor try the following DOS command before starting HamComm:

                 mode bw80

         The  'mode'  program is supplied with MS-DOS and is used here
         to switch to black and white mode.


         7.  Config file HC.CFG

         When  HamComm  is  started the program automatically searches
         for  a  configuration  file  called  "HC.CFG".   The  current
         directory is searched first, then all other directories along
         the  current  "PATH".   The  supplied HC.CFG file is an ASCII
         text file and can be sent to a printer or changed with a text
         editor.   Please  take the time to read it carefully and make
         the  required  adjustments  for  your  system.   At least you
         should substitute DL5YEC with your own callsign.

         HC.CFG  includes  explanations and examples for all available
         configuration  commands.   It  is  only special in that it is
         executed  automatically  on  program  startup.   You can also
         write your own .CFG files and execute them from the FILE menu
         while  running  HamComm.   This  could be used to set several
         parameters like baud and shift to special values in one step.
         You could also build a set of .CFG files for loading standard
         texts  in different languages.  In combination with the macro
         keys they could then be loaded with a single key.


         8.  Screen layout

         HamComm  has an SAA-like user interface with pull-down menus,
         dialog  boxes  and online helptexts.  The menu bar at the top
         of  the screen is always visible while the display is in text
         mode.   The  bottom  line has information about the currently
         selected menu item.

         Every  name  on  the  menu  bar  has a highlighted character.
         Press  and hold the ALT key and type that character to select
         the  corresponding  menu.   The  cursor-left and cursor-right
         keys  can  now  be  used to switch to the previous/next menu.
         Use the cursor-up and cursor-down keys to move to the desired
         function and hit the ENTER key.

         Every  menu  line  also  has a highlighted character.  Typing
         that character (without the ALT key) will get you directly to
         the corresponding function.


                                     - 4 -


         HamComm 2.3                Manual              February 5th 1994


         Some  frequently  used  menu  entries  have  been assigned to
         function  keys.   The  F8 key for example activates the SCOPE
         function.

         The  ESC  key  can  be  used  at  any  time to abort the menu
         selection.


         9.  Help system

         The  ALT-H  and  F1  keys both start the help system but show
         different  kinds  of  information.   The  ALT-H  key displays
         general  information about the program, the F1 key displays a
         help text specific to the current situation.


         10.  Interface schematics

         The  interface  schematics  are  included  in the online help
         texts.

         1. Start the program,
         2. Hit ALT-H to start the help subsystem,
         3. Hit the letter 'O' to select topic 'Overview',
         4. Hit the TAB key to select topic 'Converter' and hit return,
         5. Scroll the help text using the cursor-up/cursor-down keys
            and read the text.

         Hit ESC to leave the help system.

         See also appendix A for a plain ASCII version.


         11.  Receive circuit

         The  operational amplifier (OpAmp) is used to bring the audio
         signal  from  the  receiver  up  to  RS232 level.  The supply
         current  is  drawn  from  the  DTR and RTS pins of the serial
         port.   The  four  diodes  (1N4148 or similar) of the receive
         circuit form a standard bridge rectifier.  The 1uF capacitors
         are used for buffering.

         The  input  signal amplitude should be at least 100mVpp.  The
         100nF  capacitor  removes  any DC bias.  Since the OpAmp runs
         with  maximum gain there will be a (more or less) rectangular
         waveform  at  its  output.  It should have an amplitude of at
         least +/-5V to reliably drive the RS232 input.




                                     - 5 -


         HamComm 2.3                Manual              February 5th 1994


         The  operational  amplifier  LM741  was choosen because it is
         inexpensive   and  widely  available.   However  with  todays
         technology its electrical characteristics are not impressive.
         An LF356 or TL071 for example is much faster and has a higher
         input  resistance.   If  you  want  to substitute a different
         opamp  type,  keep  in  mind  that  the  serial port can only
         deliver a supply current of a few milliamperes.


         12.  PTT circuit

         The  RTS  output  of the COM port is not only used to provide
         the  supply  current  for  the  opamp,  but  also  to key the
         transmitter.   A Diode is used to protect the base of the PTT
         transistor  against the negative voltage of the RTS output in
         receive  mode.   The  resistor  is required to limit the base
         current.   In  transmit  mode  the  RTS  and  DTR pins change
         polarity.   RTS  is now positive and the transistor pulls the
         PTT  line  to  ground.   This circuit has been tested with an
         FT747, FT757GXII and a TS440S.  On some old rigs there may be
         a  high voltage on the PTT line.  The required current to key
         the  transmitter may also be too high for a small transistor,
         so better check BEFORE connecting it to the computer.


         13.  Transmit circuit

         AFSK  tone  signals  for  transmission  are  available at two
         places:

                 1. at the speaker connector
                 2. at the serial port.

         With  many  motherboards one side of the speaker is connected
         to  the  +5Volt  supply  thru  a  resistor, the other side is
         pulled  to ground by a transistor.  In contrast to most other
         areas  of  the  PC's hardware there is no standard design for
         the  speaker  output, so there may be variations.  In general
         one  side of the speaker will be near ground or +5Volt, while
         the  other side has a square-wave signal.  This signal is fed
         to two R/C filters to smooth it out.  The microphone input is
         very sensitive so a variable resistor is used for attenuation
         and a capacitor to remove any DC.








                                     - 6 -


         HamComm 2.3                Manual              February 5th 1994


         If  you  don't want to make any modifications to the PC or if
         the  speaker  output  is  not accessible, you can also get an
         AFSK   signal  from  the  TxD  pin  of  the  COM  port.   The
         frequencies  are  not  quite  as  accurate  as at the speaker
         output  and will often deviate by 5 to 10Hz, but this usually
         gives  no  problems.  The signal level at the TxD pin is much
         higher  than  at  the speaker output, so you probably have to
         change  the  component  values  for  the  R/C  filter and the
         attenuator a bit.


         14.  External converter

         An  option  "External Converter" is available on the "Keying"
         menu.   It can also be controlled by the ALT-F9/ALT-F10 keys.
         If  this  option  is  enabled,  a  mark/space  signal from an
         external  converter  or modem chip is expected at the CTS pin
         of  the  COM  port.  Please note that the normal interface is
         still  required.   There  will  be  no reception if it is not
         connected  or doesn't get the audio signal from the receiver.
         Connect  the  input  of  the  converter  and the input of the
         HamComm interface in parallel to the receiver output.

         Filter   converter   for   RTTY   are  normally  designed  to
         differentiate  between two tones.  For CW reception a kind of
         tone decoder is required that can tell the tone from noise.


         15.  External AFSK

         AFSK  tones  for  transmission  are normally available at the
         speaker  output or the TxD pin of the COM port.  If you don't
         want  to  use those signals for whatever reason, you can find
         an  FSK  signal  at  the  DTR  pin of the COM port.  For RTTY
         transmission  DTR  is  negative for 'mark' state and positive
         for  'space' state.  In CW mode DTR is negative for 'no-tone'
         and  positive  for  'tone'.   During  reception DTR is always
         positive.

         Note  that in receive mode the RTS pin is negative and always
         positive  during  transmissions.  It can thus be used to gate
         the DTR signal for keying a transmitter in CW mode.

         If  you attach any additional components to these pins please
         keep  in  mind  that the DTR/RTS signals supply the power for
         the OpAmp.





                                     - 7 -


         HamComm 2.3                Manual              February 5th 1994


         16.  Signal decoding

         The  amplified  audio  signal  is  connected to the DSR modem
         status  input  of  the  serial port where every zero crossing
         generates  an interrupt.  HamComm determines the time between
         successive interrupts using the PCs timer chip and calculates
         the   corresponding   tone   frequency.   Due  to  the  timer
         resolution  of  about  one  microsecond  the  result is quite
         accurate  and  constitutes  the  base  for all further signal
         processing.

         For  RTTY  decoding  the  tone  is  compared to the currently
         selected  center  frequency to decide wether this is a 'mark'
         or  'space'  signal.  The mark/space signal is sampled at the
         proper time according to the current baud rate collecting all
         bits of a character.

         For  CW  decoding  the  program has to differentiate the tone
         from noise.  To be regarded a valid signal the tone has to be
         between  the  currently selected mark/space frequencies for a
         certain  amount  of  time.   The program maintains a floating
         average  of  the  length  of the dots and dashes to adjust to
         varying speeds.

         When  the character is complete it is converted to ASCII code
         and displayed in the RX window.


         17.  Macro keys

         A  macro  key  can  be  used  to replay a previously recorded
         sequence  of  keystrokes.   The  digits on the top row of the
         keyboard  are  used  as  macro  keys  while  the  ALT  key is
         depressed.    They  are  normally  located  right  above  the
         QWERTY...   row.   Do not confuse these keys with the numeric
         keypad!

         In  the  beginning  there  are  no keystrokes assigned to the
         macro  keys, so pressing ALT-1, ALT-2...ALT-9 or ALT-0 has no
         effect.   To  start  recording,  select item 'Macro recorder'
         from  the  FILE  menu.   A message box will appear confirming
         that  recording has been started.  When the ENTER key is hit,
         the  message  box  will  go  away  and  from now on up to 250
         keystrokes  will be recorded along with normal processing.  A
         blinking  "! RECORDING !" message is shown at the lower right
         corner of the screen to remind you that the recorder is still
         active.




                                     - 8 -


         HamComm 2.3                Manual              February 5th 1994


         Now hit one of the macro keys to stop recording and to assign
         the  keystroke  sequence to that key.  This also replaces any
         previous  assignment.   A  message box will appear to confirm
         that  macro  recording  has terminated.  Every time the macro
         key  is  hit the recorded keystroke sequence will be replayed
         just like it had been typed again.

         To  terminate  recording  without changing any macro key just
         select  'Macro recorder' again from the FILE menu.  A message
         box  will  appear  to  confirm  that macro recording has been
         canceled.

         To  clear  a  macro  key start recording in the usual way and
         directly  after  that  hit the key to clear.  This will erase
         any  previous  recording assigned to that macro key.  Again a
         message box will confirm the result.


         18.  Macro files

         Macro  definitions  can be saved to a file by selecting "Save
         macros"  from  the FILE menu.  The usual file select box pops
         up  with  a suggested .MAC file type.  All recorded keystroke
         sequences will be saved to the selected file.

         To  load a .MAC file select "Load macros" from the FILE menu.
         All  macro  definitions  found  in  the selected file will be
         added to or replace the current assignments.  Macro keys that
         didn't  hold any keystrokes at the time the file was written,
         will not be changed when the file is loaded.

         There  is  also  a  way  to automatically load your favourite
         macros  definitions.  When HamComm is started it searches for
         the   default   macro  file  HC.MAC,  first  in  the  current
         directory, then in every directory along the PATH.


         19.  SHIP/SYNOP decoder

         Weather  reports  are  transmitted by many stations troughout
         the world, 24 hours a day.  If you live in europe try to copy
         Quickborn  Meteo  (near  Hamburg,  Germany) on 4583, 7646 and
         11638kHz, or Bracknell (UK) around 4488kHz.  In north america
         try  CFH (Halifax, Nova Scotia) on 4271, 6496.5 and 10536kHz.
         There   are   many   others   between   4000   and   5000kHz.
         Transmissions  are  normally in Baudot, 425Hz shift, 50 or 75
         baud.




                                     - 9 -


         HamComm 2.3                Manual              February 5th 1994


         The SYNOP format is used for reports from land stations, SHIP
         format  is  used  for  reports  from ships and other maritime
         vessels.   The  messages include data about temperature, wind
         speed/direction,   cloud   cover,  precipitation,  dew-point,
         pressure  and other meteorological information.  SHIP reports
         also include the current position of the vessel.

         Land  stations are identified by a five-digit station number.
         These  are  fixed stations, so their geographical position is
         not  transmitted  with  a SYNOP report.  To give you a better
         idea  where  the  reporting station is located, HamComm comes
         with  a  list  of  about  10000  station  numbers,  names and
         geographical  position.   The program will automatically pick
         the  correct  entry  from  this  list  while decoding a SYNOP
         report.

         A typical message looks like this:

         zczc 548
         sien42 edzw 141500
         aaxx 14154
         01465 42889 42715 10084 20022 40159 52033 81048=
         02060 41480 40000 11088 21113 40060 52035 72272
         83530 333 83694=
         nnnn

         This  is  what you get if the SHIP/SYNOP decoder ist switched
         off.

         The   first  line  of  a  message  starts  with  zczc  and  a
         three-digit transmission sequence number.  The second line is
         a header describing the following information.  Here 'sien42'
         indicates  a  "synoptic  report  at  intermediate  hours" for
         northern  europe,  'edzw'  is  the  international four-letter
         location  indicator  of  the station originating or compiling
         the  bulletin  and  '141500'  means  3pm UTC on day 14 of the
         current  month.   'aaxx'  is the indicator for SYNOP reports,
         'nnnn' marks the end of a message.

         There  are  other  formats  in  use  for  different  kinds of
         information.   Currently  HamComm  only  supports decoding of
         SHIP  and  SYNOP  reports.  A message may contain one or more
         reports separated by = characters.  Explaining the reports in
         detail is beyond the scope of this manual.







                                    - 10 -


         HamComm 2.3                Manual              February 5th 1994


         With the WX decoder switched on (from the TEXT menu) the same
         message looks like this:

         zczc [start] 548 [message 548]
         sien42 [Synoptic reports at intermediate hours (SYNOP, SHIP)]
          [Northern Europe]
          edzw [Offenbach (MET/COM Centre)]
          141500 [day:14 UTC:1500]
         aaxx [SYNOP]
          14154 [day:14 UTC:1500]
                [Wind speed obtained from anemometer (knots)]

         01465 [Norway, 58ø24'N 008ø48'E TORUNGEN (LGT-H)]
          42889 [manned] [cloud height:2000-2500m] [visibility:75km]
          42715 [cloud cover:4/8] [wind dir:270 deg, speed:15]
          10084 [air temp:+8.4]
          20022 [dew-point temp:+2.2]
          40159 [pressure at sea level:1015.9hPa]
          52033 [pressure:increasing] [change in 3h:3.3hPa]
          81048 [cloud info]

         =
         02060 [Sweden, 68ø41'N 021ø32'E NAIMAKKA]
          41480 [manned] [cloud height:300-600m] [visibility:30km]
          40000 [cloud cover:4/8] [wind dir:calm, speed:0]
          11088 [air temp:-8.8]
          21113 [dew-point temp:-11.3]
          40060 [pressure at sea level:1006.0hPa]
          52035 [pressure:increasing] [change in 3h:3.5hPa]
          72272 [past wx: snow, or rain & snow mixed,
                          cloud cover > 1/2 of sky]
                [wx now: Snow]
          83530 [cloud info]
          333 [section 3]
          83694 [clouds:3/8, stratocumulus, 1000-1500m]

         nnnn [EOM]

         HamComm  displays  the  incoming text just as before.  The WX
         decoder  watches  the  characters  go by, waiting for certain
         keywords  like zczc (start of msg), aaxx (SYNOP report), bbxx
         (SHIP  report)  and  nnnn (end of msg) to synchronize with an
         incoming  message.   If  it  thinks it knows what the text is
         about,  it  starts  to  insert  comments.   The  comments are
         surrounded   by   square   brackets   and   therefore  easily
         distinguished  from  the  normal  text  (there  are no square
         brackets in the Baudot character set).




                                    - 11 -


         HamComm 2.3                Manual              February 5th 1994


         There are other ways to build a SHIP/SYNOP decoder.  It could
         collect  all data for a report and then display the result in
         a  nicely  formatted  way.  However, there is a problem.  The
         kind of RTTY transmission used for these reports has no error
         correction,   not   even   error  detection.   It's  hard  to
         automatically  classify  a  message  as  ok  or garbled.  For
         example: if the program says there are +30 degrees celsius in
         Greenland and it's december, you will hopefully not buy that.
         HamComm  has  no idea where Greenland is and not the foggiest
         about  the  climate  there,  so  it  can't catch that type of
         error.

         The  program  displays  the incoming text as received, so you
         can  see  if there is garbage coming in.  Usually it is quite
         obvious  if the input is bad.  With a WX decoder working like
         a 'black box' it is sometimes very hard to see how it came to
         its conclusions and what to believe or not.


         20.  Scope function

         In  RX  mode  the tone decoder routine calculates the current
         signal  frequency for use by other parts of the program.  The
         SCOPE  function  uses  this  value  to display a graph of the
         input  frequency  vs.   time.   This  is the blue line on the
         SCOPE screen.

         The tone decoder also maintains a floating average frequency.
         The  effect  is very similar to a low-pass filter and is used
         for  noise  reduction.  The result is displayed at the top of
         the screen as a red line.

         The  solid  green  line  marks  the currently selected center
         frequency  and the dotted lines above and below show the mark
         and  space  tones.  For RTTY reception the center line should
         be  in  the  middle between the mark and space tones.  For CW
         reception  the signal should match the center frequency.  All
         signals  outside  the  area  marked  by  the dotted lines are
         ignored.












                                    - 12 -


         HamComm 2.3                Manual              February 5th 1994


         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menu bar
                      ESC  same as F10
                      '+'  toggle display of decoded signal
                      '*'  toggle grid display
                      'B'  toggle position of red line
                     HOME  reset sample rate to 1ms
                    PG-UP  sample rate faster
                  PG-DOWN  sample rate slower
                    ENTER  hold display immediately

         The  right  mouse  button holds the display at the end of the
         current  sweep.  The left mouse button activates the menu bar
         just like F10.

         The  red  line  (input  signal  after  low-pass)  is normally
         displayed  at the top of the screen to not interfere with the
         blue  line.   In its second position it will overlay the blue
         line to compare the two signals.

         Display  of  the decoded signal is normally disabled.  It can
         be found at the bottom of the screen and shows the mark/space
         states for RTTY and tone/no-tone states for CW reception.

         With  some  practice it is quite easy to determine the signal
         you  are  listening  to  by  watching the SCOPE display.  CW,
         AMTOR   ARQ  and  FEC,  Packet  Radio  and  RTTY  show  their
         characteristic  patterns and you can also watch unstable VFOs
         sweeping slowly across the band.


         21.  Spectrum function

         On  entry  to the Spectrum function a graphics mode according
         to the video card and monitor in use is activated.

         Every  millisecond  the  current  input frequency is checked.
         For  every  frequency  there  is  a  counter and the one that
         corresponds  to  the  current  frequency is incremented.  All
         counter  values  are  displayed  as  vertical lines with each
         sweep  from  left to right.  The higher the count, the longer
         the  line.   What  you see on the screen is therefore not the
         true  audio spectrum but the result at the output of the tone
         decoder  routine.   An  opamp  and  a few lines of code can't
         substitute a real spectrum analyzer.




                                    - 13 -


         HamComm 2.3                Manual              February 5th 1994


         When set to 1Hz per pixel SPECTRUM has the best resolution of
         all display functions.  For example, the actual shift used by
         an RTTY station can be determined quite accurately.

         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menu bar
                      ESC  same as F10
                      '-'  toggle raw/filtered data
                      '+'  toggle 'shaddow' (color displays only)
                      '*'  toggle dot/line mode
                     HOME  reset, start at 200Hz, 3Hz per pixel
                    PG-UP  zoom in
                  PG-DOWN  zoom out
                     LEFT  lower frequencies
                    RIGHT  higher frequencies
                    SPACE  clear display
                    ENTER  hold display

         The  right  mouse  button holds the display at the end of the
         current  sweep.  The left mouse button activates the menu bar
         just like F10.

         If  you  have a slow PC then don't use the SPECTRUM function,
         you  might  get  frustrated.   There  simply isn't enough CPU
         power  to keep the display in motion.  AT class maschines and
         real fast XTs should be ok.

         The   SPECTRUM   function   has   been   found  to  be  quite
         entertaining, especially with a color display.  Next time you
         got  visitors  in  your  shack who don't know what's going on
         just  start  this  function,  turn  the  lights low and sweep
         across a crowded band.

















                                    - 14 -


         HamComm 2.3                Manual              February 5th 1994




         22.  Bitlength statistics

         The  BITLENGTH function is a graphics display of the MARK and
         SPACE pulse length as detected by HamComm.  It's main purpose
         is to quickly get an idea about the speed of the signal.

         With every transition of the decoded MARK/SPACE signal a high
         or  low  pulse  ends.   The  upper  histogram shows the pulse
         duration  statistics  of the high pulses, the lower histogram
         shows the statistics of the low pulses.

         Before  using  this function the center frequency must be set
         to the center between the MARK and SPACE tones, otherwise the
         pulse width display will suffer from distortion.

         The  shortest  pulses of an RTTY signal are normally equal to
         the length of one bit.  Therefore the leftmost peak indicates
         the  baud  rate  of  the  incoming  signal.   A  noisy signal
         produces  lots  of  short spikes.  They tend to accumulate at
         the  left end of the histogram and should be ignored for baud
         analysis.

         The  BITLENGTH  function tries to identify the leftmost valid
         peek  automatically,  but  this  may fail with noisy signals.
         Below  each  histogram  the  baud  rate  corresponding to the
         highest  peak  is displayed.  There is also a MARKER that can
         be moved freely using the LEFT and RIGHT keys.

         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menu bar
                      ESC  same as F10
                    PG-UP  zoom in
                  PG-DOWN  zoom out
               LEFT,RIGHT  move marker
             CONTROL-LEFT  move marker, fast mode
            CONTROL-RIGHT   "     "      "    "
                    ENTER  hold display

         The  marker  can also be controlled by moving the mouse while
         holding  down  the  right  mouse  button.   The  baud  number
         corresponding  to  the  marker  position  is displayed at the
         upper left corner of the screen.

         The left mouse button activates the menu bar just like F10.



                                    - 15 -


         HamComm 2.3                Manual              February 5th 1994




         23.  Converter checkout

         So  you  have  build  the  interface  and made the neccessary
         connections  to  the  radio.  You fire up the program and you
         see - nothing.

         To  find  out  what  is going wrong let's start at the serial
         port.  HamComm needs to know two parameters about a COM port:

          1. the port address
          2. the IRQ number

         The  port  address  and  IRQ  number  for  COM1  and COM2 are
         standardized  and  therefore  predefined  in  HC.CFG  to  the
         following values:

                     addr   IRQ
              COM1   3F8h    4
              COM2   2F8h    3

         For other serial ports there is no real standard, so COM3 and
         COM4 are not defined in the supplied HC.CFG.  Undefined ports
         can not be selected from the PORT menu.


         24.  Port address

         Start  the  program  and select entry 'HamComm' from the INFO
         menu.  A small window appears displaying, among other things,
         the  port  address  and IRQ of the serial ports as defined in
         HC.CFG.   If  the  values  for the port you want to use don't
         match the hardware, correct HC.CFG with a text editor.

         Remove  the  interface for now.  Select the correct port from
         the  port  menu,  then  hit  F3 to activate the RX/TX screen.
         Using a voltmeter check the RTS and DTR outputs of the serial
         port with respect to the GND pin.  RTS should have a negative
         voltage and DTR should be positive.

         Now  switch to transmit (TX) mode.  This can be done from the
         MODE  menu  but it's easier to hit control-T.  When switching
         to  TX  mode  both RTS and DTR reverse their polarity, so RTS
         should now be positive and DTR should be negative.






                                    - 16 -


         HamComm 2.3                Manual              February 5th 1994


         If they don't, here is a list of what might be wrong:

          - the voltmeter is broken.

          - you are measuring at the wrong socket.
            The serial ports of a PC are normally
            25-pin or 9-pin male SUB-D sockets.

          - you are measuring at the wrong pins.

                      4     7                              4   5
                     RTS   GND                            DTR GND
            ----1-----|-----|-----------13---     ----1-----|-|----
            \         |     |               /     \         | |   /
             \  o o o o o o o o o o o o o  /       \  o o o o o  /
              \  o o o o o o o o o o o o  /         \  o o o o  /
               \             |           /           \   |     /
                14-----------|---------25             \6-|---9/
                            DTR                         RTS
                             20                          7

          - you have selected the wrong com port. Check the PORT menu.

          - the port address as defined in HC.CFG for this port is not
            correct.  Check the INFO menu and HC.CFG.

          - the com port has a different address from what you think.
            The address can often be selected with jumpers on the
            serial card.  Check the documentation for your computer.
            On some newer PCs and notebooks the com port address can
            be changed or the port can be disabled with a setup
            program.

          - if only one of the signals (RTS or DTR) changes polarity,
            the line driver for the other signal may be broken.
















                                    - 17 -


         HamComm 2.3                Manual              February 5th 1994




         25.  Op-Amp power supply

         Now  let's  take  a  look  at the interface.  By far the most
         common problems are:
          - wrong or missing connections
          - solder bridges and cold solder joints

         If  you think the problem is with the interface take the time
         and carefully inspect it under a magnifying glass.

         If that doesn't work, proceed as follows.

         Switch  off  the  computer  and  connect the interface to the
         serial  port.  Don't connect it to the radio yet, connect the
         audio  input  to  GND.   If  possible the interface should be
         directly  plugged  to the com port.  Any cable between the PC
         and  the  interface  should  be  avoided,  it may degrade the
         signal quality.

         Switch  the  PC on, start HamComm, select the right port from
         the  PORT  menu  and hit F3 for the RX/TX screen.  Check that
         RTS  and DTR still change polarity when you toggle between RX
         and TX mode.

         Check  the supply voltages at the op-amp with respect to GND.
         The  positive  voltage  at pin 7 should be +5V or higher, the
         voltage at pin 4 should be -5V or lower (more negative).

                         +V out
                       8  7  6  5
                       |  |  |  |    Operational Amplifier
                     |------------|
                     |            |  LM741 or TL071
                     |            |
                     |-|          |  DIL-8 package, top view
                       |          |
                     |-|          |   +V = positive supply
                     |            |   -V = negative supply
                     |            |   -I = inverting input
                     |------------|   +I = non-inverting input
                       |  |  |  |    out = output
                   Pin 1  2  3  4
                         -I +I -V

         Check  the  voltages  both  in  RX and TX mode at the op-amp.
         Here they should NOT change polarity, otherwise the IC may be
         permanently  damaged.   If  they do or if the readings change
         significantly  in  RX  and  TX  mode,  check  the  wiring and

                                    - 18 -


         HamComm 2.3                Manual              February 5th 1994


         polarity  of  the  four diodes between the PC and the op-amp.
         Also check the two capacitors used for buffering the supply.

         Although  only  a current of a few milliamperes is needed for
         the  op-amp,  some  com  ports  can  not deliver the required
         supply  voltages.   You  may try to find an op-amp that draws
         less  current  but  the easiest solution is to use two 9-Volt
         batteries:
                                 bat 1      bat 2

                                  ||         ||
                 op-amp pin 7 <---||---GND---||---> op-amp pin 4
                                 +||-       +||-


         If  the power supply is ok we will now try to find out if the
         op-amp  works  correctly.   First  check  the  voltage at the
         inverting  and  non-inverting  inputs.  Both should read 0 or
         VERY  close  to  0 volts with respect to GND.  If they don't,
         there is probably a wiring error or the chip is broken.

         Temporarily  connect a resistor of about 1M (megaohm) between
         the  non-inverting input (pin 3) and the positive supply (pin
         7).   Be  very  careful  not to short any pins.  The op-amp's
         output  should  go  as  high  as it can go, which is normally
         about 1 volt below the positive supply.

         Remove  the resistor and connect it between the input (pin 3)
         and the negative supply (pin 4).  The output should now be as
         low as it can go, about 1 volt above (more positive) than the
         negative supply.

         Check  the  output  signal directly at the DSR pin of the com
         port to make sure that the wiring is ok.  This is only a very
         simple  test  wich  the  op-amp will only fail if it is badly
         damaged.

         The  output  of  the  op-amp  will also be positve or negativ
         without  the  resistor.  This is normal and doesn't mean that
         the chip is broken.











                                    - 19 -


         HamComm 2.3                Manual              February 5th 1994


         26.  IRQ number

         Now connect the input of the interface to the audio output of
         the  receiver.  The op-amp is quite sensitive and should work
         even  with very low signals.  Some radios have a socket for a
         tape  recorder  where  the  amplitude  is  independent of the
         volume setting.  Try that first.

         Tune in to some strong signal, preferably to a constant tone.
         At  the  DSR pin of the com port there should now be a square
         wave  signal.   The amplitude at DSR should have at least the
         +/-5V swing required to reliably drive an RS-232C input.

         Start  HamComm  to  check  if  the  signal  at  DSR generates
         interrupts.  Select the right port from the PORT menu and try
         the TUNE, SCOPE or SPECTRUM function from the MODE menu.

         If  all  of  these functions seem to be dead, HamComm doesn't
         get  any  hardware  interrupts  from the serial port.  Select
         entry  'HamComm'  from  the INFO menu and check the displayed
         IRQ  number  for  the  port  you want to use.  If it's wrong,
         specify the right one in HC.CFG.

         Make  sure  that  the  port  really uses the IRQ you think it
         does.   Many  serial cards have jumpers or small switches for
         IRQ line selection.  Some newer PCs and notebooks can do this
         from a setup program.

         Please  note, that an IRQ line can only be used by one device
         at  a  time.   For  example, if you have a mouse on IRQ 4 you
         can't use a COM port on the same IRQ at the same time.




















                                    - 20 -


         HamComm 2.3                Manual              February 5th 1994




         27.  Appendix A - Interface schematics

                                                              RS-232C
                       Receive Circuit                         25  9
                                                              pin pin
                                                  D1
                           LM741-------*--------*-I<--*--> DTR 20   4
                                |      |        | D2  |
                           3 |\ |      |      ---->I---
           >------||---*-----|+\ 7     |      | |
                  C1   |     |  \______|______|_|________> DSR  6   6
                0.1uF  |   2 |  /6     |      | | D3
                       |  ---|-/       |      | --I<--
         Signal        |  |  |/ |4     |      |   D4  |
         from          /  /     ---*---|------*--->I--*--> RTS  4   7
         Receiver    R1\  \R2      |   |              |
                   100K/  /100K    |   | +            |
                       \  \       === ===  C2,C3      |
                       |  |       === ===  1 uF       |
                       |  |     +  |   |   16V        |
           >-----------*--*--------*---*--------------|--> GND  7   5
                                   |                  |
         PTT Circuit               |E                 |
         (omit for receive-only)   ^\      R3         |  D1-D5
                       Q1            \I    1K     D5  |  1N914 or
                       2N2222         I---/\/\----I<--|  1N4148
                                     /I B
         PTT <----------------------/
                                      C


          Transmit Audio Circuit    R2         R3
          (omit for receive-only)   15K        15K
                       --------*---/\/\---*---/\/\----*----<  Out
               C1      |       |          |        R4 |
               .1 uF   / R1    |          |       220K\
          <----| |---->\ 10K  === C2     === C3       /     PC Speaker
           MIC         / var. === .022   === .022     \
           Out         |       |  uf      |  uF       |
          <------------*-------*----------*           *----<  +5V
                                          |
                                         GND







                                    - 21 -


         HamComm 2.3                Manual              February 5th 1994




         28.  Appendix B - Key assignment summary

         --- All Windows ---

         F1              display help text
         F2              RX/TX window, CW mode
         F3              RX/TX window, Baudot mode
         F4              RX/TX window, ASCII mode, 7 bit
         F5              RX/TX window, ASCII mode, 8 bit
         F6              Bitlength display
         F7              Spectrum display
         F8              Scope display
         F9              Tune window
         F10             Menu bar

         ALT-1           execute macro 1
         ALT-2           execute macro 2
         ALT-3           execute macro 3
         ALT-4           execute macro 4
         ALT-5           execute macro 5
         ALT-6           execute macro 6
         ALT-7           execute macro 7
         ALT-8           execute macro 8
         ALT-9           execute macro 9
         ALT-0           execute macro 0

         ALT-F4          Terminate programm
         ALT-F5          WX decoder off
         ALT-F6          WX decoder on
         ALT-F7          AFC off
         ALT-F8          AFC on
         ALT-F9          external converter off
         ALT-F10         external converter on

         ALT-C           Callsign decoder
         ALT-X           Terminate programm


         --- TUNE Window ---

         HOME            reset center frequency
         LEFT            decrease center frequency
         RIGHT           increase center frequency






                                    - 22 -


         HamComm 2.3                Manual              February 5th 1994


         --- RX/TX Window ---

         SHIFT-F1        Standardtext 1
         SHIFT-F2        Standardtext 2
         SHIFT-F3        Standardtext 3
         SHIFT-F4        Standardtext 4
         SHIFT-F5        Standardtext 5
         SHIFT-F6        Standardtext 6
         SHIFT-F7        Standardtext 7
         SHIFT-F8        Standardtext 8
         SHIFT-F9        Standardtext 9
         SHIFT-F10       Standardtext 10

         LEFT            move TX cursor left, 1 character
         RIGHT           move TX cursor right, 1 character
         UP              move TX cursor up, 1 line
         PAGE-UP         move TX cursor up, 1 page
         DOWN            move TX cursor down, 1 line
         PAGE-DOWN       move TX cursor down, 1 page
         HOME            move TX cursor to first line
         END             move TX cursor to last line
         INSERT          toggle insert mode on/off
         DELETE          delete character under cursor
         BACKSPACE       delete character left to cursor
         TAB             toggle NORMAL/REVERSE keying direction
         ENTER           transfer text line to transmit buffer

         CONTROL-A       move TX cursor to beginning of line
         CONTROL-D       insert time and date
         CONTROL-E       move TX cursor to end of line
         CONTROL-F       open/close logfile
         CONTROL-H       same as BACKSPACE
         CONTROL-I       same as TAB
         CONTROL-L       toggle AutoUnshift on/off
         CONTROL-M       same as ENTER
         CONTROL-P       toggle transmit monitoring on/off
         CONTROL-S       send textfile
         CONTROL-T       toggle transmit/receive mode
         CONTROL-W       toggle Line/Word mode
         CONTROL-X       clear TX line
         CONTROL-Z       insert time

         CONTROL-LEFT    roll RX window backwards, 1 line
         CONTROL-HOME    roll RX window backwards, 1 page
         CONTROL-RIGHT   roll RX window forewards, 1 line
         CONTROL-END     roll RX window forewards, 1 page
         CONTROL-PAGE-UP resize RX/TX window
         CONTROL-PAGE-DOWN "      "     "



                                    - 23 -


         HamComm 2.3                Manual              February 5th 1994


         --- SCOPE Display ---

         ESCAPE          same as F10
         '+'             toggle display of decoded signal
         '*'             toggle grid display
         'B'             toggle position of red line
         HOME            reset sample rate to 1ms
         PAGE-UP         sample rate faster
         PAGE-DOWN       sample rate slower
         ENTER           hold display immediately


         --- SPECTRUM Display ---

         ESC             same as F10
         '-'             toggle raw/filtered data
         '+'             toggle 'shaddow' (color displays only)
         '*'             toggle dot/line mode
         HOME            reset, start at 200Hz, 3Hz per pixel
         PAGE-UP         zoom in
         PAGE-DOWN       zoom out
         LEFT            lower frequencies
         RIGHT           higher frequencies
         SPACE           clear display
         ENTER           hold display


         --- BITLENGTH Display ---

         ESC             same as F10
         PAGE-UP         zoom in
         PAGE-DOWN       zoom out
         LEFT            move marker left
         RIGHT           move marker right
         CONTROL-LEFT    move marker left, fast mode
         CONTROL-RIGHT   move marker right, fast mode
         SPACE           clear display
         ENTER           hold display













                                    - 24 -


         HamComm 2.3                                             Index


         AFSK output................6
         Bitlength.................15
         CGA........................2
         Converter, external........7
         Converter..................5
         Converter.................16
         CW.........................8
         Desqview...................2
         EGA........................3
         ESC........................5
         Exclusion of warranty......2
         External AFSK..............7
         external converter.........7
         F1.........................5
         Floppy.....................2
         Function keys..............5
         Harddisk...................2
         HC.CFG.....................4
         Help system................5
         Installation...............3
         Interface schematics.......5
         Interface.................16
         Introduction...............1
         Laptop.....................4
         LCD........................4
         License....................1
         Macro files................9
         Macro keys.................8
         Menu bar...................4
         Multitasking...............2
         Operational Amplifier......5
         PTT circuit................6
         Receive circuit............5
         RTTY.......................8
         Scope function............12
         Screen layout..............4
         Selection..................4
         SHIP/SYNOP.................9
         Signal decoding............8
         Speaker....................6
         Spectrum function.........13
         Startup....................3
         SuperVGA...................3
         System requirements........2
         Transmit circuit...........6
         VGA........................3
         Video adapter..............2
         Windows....................2
         XT.........................2


                                       i