6. CONFIG: how to configure UC
==============================

When UC is started without parameters there is the option to configure
UC (by pressing the 'C' key).

General options are:

   A -> Default compression method
   B -> Default operation
   C -> Reliability level
   D -> Automatic archive conversion
   E -> Virus scan during conversion
   F -> Smart skipping
   G -> Amount of output/information
   H -> Show (multimedia) banners
   I -> Store OS/2 2.x extended attributes
   J -> Store system/hidden files

System options are:

   M -> Video mode
   N -> Dynamic program swapping
   O -> Use EMS
   P -> Use XMS
   Q -> Use 386/486/Pentium features
   R -> Advanced networking
   S -> Location for temporary files
   T -> Location for manuals (*.DOC)
   U -> Location for error logfile
   V -> Loc. for batch&script files

Quick setup options are:

   1 -> default
   2 -> max speed
   3 -> max compress
   4 -> max safe
   5 -> UNDO

The configuration you chose here will be your default configuration
when using UC. Some of the options in the configuration screen can
also be temporary set on the command line. The command line options
are also described in this document.

This document contains the following paragraphs:

        - A. General options
        - B. System options
        - C. Quick setup
        - D. Batch files
        - E. Optimizing performance

To jump to a certain paragraph, press the corresponding letter. To
jump to a specific document/chapter, press the corresponding digit.
See chapter 1 paragraph E for an overview of all documentation.


6.A GENERAL OPTIONS.
====================

A -> Default compression method
-------------------------------
   Equivalent command line options: -TN, -TT, -TF

   The compression type can be NORMAL, TIGHT/MULTIMEDIA or FAST. When
   installing UC the default compression type is normal.

   In TT mode, UC will detect whether a file is a multimedia file.
   Special (lossless) multimedia compression will then take place.

B -> Default operation
----------------------
   Equivalent command line options: -I, -B

   The add operation can be in BASIC MODE or INCREMENTAL MODE. In
   basic mode files that already exist in the archive will be replaced
   by a new version.

   In incremental mode more versions of a file can be kept in the
   archive. When an already existing file is added to the archive, the
   newer version of the file will be added. This mode increases the
   speed of the addition significantly, especially for slow disks
   and/or large archives.

   Another advantage of the incremental mode is the possibility of
   keeping multiple versions of a file in the archive. If, for
   example, you want to see what is changed in the file, just look at
   a previous version.

C -> Reliability level
----------------------
   Equivalent command line options: !RELIA=DETECT, !RELIA=PROTECT,
                                    !RELIA=ENSURE

   The reliability level can be DETECT, PROTECT or ENSURE.

   Detect means errors will be reported, but no action will be taken.

   Protect means errors will be avoided, by using damage protection.

   Ensure mode means UC will make as sure as technically possible,
   everything will go perfect. First the existing archive will be
   tested. Then the command given will be executed. The third step
   includes a complete test on the new archive. When something went
   wrong, a 'rollback' will take place, and the original archive will
   be restored. To ensure correct storage on your harddisk, U2_FLUSH
   is called at appropriate moments during execution of your command.
   (See paragraph D.)

D -> Automatic archive conversion
---------------------------------
   Equivalent command line options: !ARCON=ON, !ARCON=OFF

   Automatic conversion of other archiver's archives can be ON or OFF.
   When the automatic conversion is on, any operation can be done on
   other archiver's archives. UC will automatically start rebuilding
   the archive to a UC archive. After rebuilding, the command will be
   executed.

   When the automatic conversion is off, UC will not automatically
   convert archives, but prompt the user, asking permission to convert
   the archive.

E -> Virus scan during conversion
---------------------------------
   Equivalent command line options: !VSCAN=ON, !VSCAN=OFF

   Virus scan can be ON or OFF during the conversion of another
   archiver's archive (also see paragraph D).

F -> Smart skipping
-------------------
   Equivalent command line options: !SMSKIP=ON, !SMSKIP=OFF

   Smart skipping can be ON or OFF.

   When smart skipping is on, unchanged files (already in the archive)
   are skipped during addition. This makes updating much faster.

G -> Amount of output/information
---------------------------------
   The amount of output/information can be MINIMAL, VERBOSE or NORMAL.

   UC shows all kinds of information while it is executing your command.
   Minimal information mode only shows the filenames being processed, no
   progress indicators are given. Verbose information mode shows in
   great detail what UC is doing, this includes small popup windows for
   diskcache activities. For instance the file name in process is
   followed by blocks indicating progress. Normal information mode shows
   what UC is doing, but does not give undue attentention to details
   which are not directly related to the given command.

H -> Show (multimedia) banners
------------------------------
   Equivalent command line options: !BAN=ON, !BAN=OFF, !BAN=ASK

   You can choose if the banners added to the archives are
   shown/played automatically (ON), only when you agree (ASK) or never
   (OFF).

I -> Store OS/2 2.x extended attributes
---------------------------------------
   Equivalent command line options: !SOS2EA=ON, !SOS2EA=OFF

   By putting this option ON, OS/2 EA's will be stored when UC finds
   any during compression, when this option is OFF UC will not store
   OS/2 2.x EA's. OS/2 2.x extended attributes (such as icons, WPS
   long icon names, WordPerfect 5.2 for OS/2 summary information etc.)
   will be retained in an archive when the option is ON. Please note
   that OS/2 2.x EA's will ALWAYS be extracted, when present in an
   archive. Extended attributes are preserved by the optimize command,
   even if this is performed on a machine which does not run OS/2.

J -> Store system/hidden files
------------------------------
   Equivalent command line options: !SYSHID=ON, !SYSHID=OFF,
                                    !SYSHID=ASK

   You can choose if you want 'system' and 'hidden' files to be added
   ON, OFF or if you want UC to ASK you how to deal with them.


6.B SYSTEM OPTIONS.
===================

M -> Video mode
---------------
   If your card is not compatible with MDA, HERCULES, CGA, EGA, VGA,
   SVGA, XGA, etc. (very unlikely but possible for some older
   computers) choose BIOS mode. If you have a monochrome monitor (or
   laptops etc.) choose MONO instead of COLOUR. Please note that if UC
   detects DesqView (which prefers BIOS video on 286 computers) it
   will use BIOS video, even if UC is not configured to use BIOS
   video.

N -> Dynamic program swapping
-----------------------------
   Dynamic program swapping can be ON (in which case UC will be
   swapped to EMS or disk if it invokes DOS) or OFF.

O -> Use EMS
P -> Use XMS
------------
   Switch EMS/XMS OFF if your EMS or XMS (emulator) is not compatible
   with the Lotus/Intel/Microsoft specifications. This is not likely
   since UC uses these very conservative.

Q -> Use 386/486/Pentium features
---------------------------------
   Switch off use of 386/486/Pentium options. This is usefull in case
   programs are active which violate 386/486/Pentium programming rules.

R -> Advanced networking
------------------------
   Equivalent command line options: !NET=ON, !NET=OFF, !NET=AUTO-SKIP

   Network Support. If you have a version of DOS which does not
   support DOS network calls (e.g. 2.0), or if you have a network
   which behaves very differently from IBM, Lantastic, Microsoft, Novell
   or Vines networks, you can set this option to OFF. Sharing archives is
   then no longer possible.

   When UC attempts to compress a locked file, it allows the user to
   skip this file by hand. When auto-skip mode is active, locked files
   will be skipped automatically. A warning is reported if files are
   skipped.

S -> Location for temporary files
---------------------------------
   The location for temporary files can be configured. When everything
   goes well you will never notice the temporary files. Please make sure
   the directory configured exists on your disk.

T -> Location for manuals (*.DOC)
---------------------------------
   UC will look for the manual files in the directory configured.

U -> Location for error logfile
-------------------------------
   The error logfile will register all errors and warnings that appear
   while executing UC.

V -> Loc. for batch&script files
--------------------------------
   UC will look for its special batch and script files in the directory
   configured.


6.C QUICK SETUP.
================

1 -> default
------------
   The default setup changes the following subjects:

       GENERAL OPTIONS:

           default compression mode        into    normal
           default operation               into    basic mode
           reliability level               into    detect
           automatic archive conversion    into    off
           virus scan during conversion    into    off
           amount of output/information    into    normal
           show (multimedia) banners       into    ask
           store OS/2 2.x ext. attributes  into    off
           store system/hidden files       into    ask

       SYSTEM OPTIONS:

           video mode                      into    colour
           dynamic program swapping        into    on
           use EMS                         into    on
           use XMS                         into    on
           use 386/486/Pentium features    into    on
           advanced networking             into    on
           all locations will be set to the same location as UC.EXE

2 -> max speed
--------------
   The max speed setup changes the following subjects:

       GENERAL OPTIONS:

           default compression             into    fast
           default operation               into    incremental
           reliability level               into    detect
           automatic archive conversion    into    on
           virus scan during conversion    into    off
           amount of output/information    into    minimal
           show (multimedia) banners       into    off

       SYSTEM OPTIONS:

           video mode   No matter whether the video mode is colour or
                        mono, this configuration will turn off BIOS usage
           use EMS                         into    on
           use XMS                         into    on
           use 386/486/Pentium features    into    on
           advanced networking             into    auto-skip


3 -> max compress
-----------------
   The max compress setup changes the following subjects:

       GENERAL OPTIONS:

           default compression             into    tight
           default operation               into    basic mode
           reliability level               into    detect
           automatic archive conversion    into    on

4 -> max safety
---------------
   The max safe setup changes the following subjects:

       GENERAL OPTIONS:

           default operation               into    incremental mode
           reliability level               into    ensure
           automatic archive conversion    into    off
           virus scan during conversion    into    on
           smart skipping                  into    off
           show (multimedia) banners       into    off

       SYSTEM OPTIONS:

           video mode   No matter whether the video mode is colour or
                        mono, this configuration will turn on BIOS usage
           use EMS                         into    off
           use XMS                         into    off
           use 386/486/Pentium features    into    off
           only if advanced networking was auto-detect:
                                           into    on

5 -> UNDO
---------
   The configuration will be reset to the state it was before you
   started the configuration screen.


6.D BATCH FILES.
================

The following batch files are described in detail:

   U2_EDIT    edit text file
   U2_CHECK   check files for viruses
   U2_FLUSH   flush harddisk cache
   U2_SHOW    show/play (GIF, MOD, JPG and TXT) banner files
   U2_EXxxx   extract all files from an archive
   U2_XTRA    perform user defined operations during conversion

You are free to edit supplied batch files, to make them call other
than the default programs. You can also add new files (e.g. U2_EXxxx)
to enhance the functionality of UC.

U2_EDIT.BAT
-----------
   Task
      This file calls your favourite editor with the file to be edited
      as parameter.

   When is it called?
      The file is used when you use the command REVISE COMMENT.

   Standard contents
      The default editor is the DOS 5.x/6.x/7.x EDIT.

U2_CHECK.BAT
------------
   Task
      This file calls virus scanner(s). The current directory and
      its subdirectories are scanned for viruses. When no viruses are
      found, the file U$~CHK3 is generated, which is used as a flag.
      (When this file is present, UC knows that no viruses are found
      and that it can continue its work.) When viruses are found, a UC
      fatal error will occur.

   When is it called?
      When virus scanning is on in the configuration, this file is
      used during conversion of archives.

   Standard contents
      Default McAffee (100 or higher) and F-PROT are called.

U2_FLUSH.BAT
------------
   Task
      Everything in the disk-cache (e.g. SmartDrive, PC-CACHE or
      Norton Cache) which is not yet written to the disk ('delayed' or
      'deferred' write cache) will be written to disk immediately.

   When is it called?
      While using UC in ensure mode, it will secure its 'transactions'
      using U2_FLUSH. This is to make sure contents of the disk are
      correct, after the completion of a transaction.

   Standard contents
      Attempts to call PC-CACHE, Norton Cache, ADCACHE and SmartDrive.

U2_SHOW.BAT
-----------
   Task
      Show/play banners while extracting files from an archive. The
      banners are in the current directory when U2_SHOW is called.

   When is it called?
      When files are extracted from an archive and banners are present
      they can be shown/played. In the configuration you can choose
      whether you want the banners to be shown/played.

   Standard contents
      First MODPLAY is called to play the .MOD banner. The VPIC is
      called to show the .GIF banner and then FullView is called to
      show the .JPG file. Finally DOS TYPE is used to show the text
      banner.

U2_EXxxx.BAT
------------
   xxx stands for ARC, ARJ, HA, HPK, HYP, LZH, PAK, UCN, ZIP, ZOO etc..

   Task
      These files are used to extract all files, from the archive to
      be converted, into the current directory. To check if everything
      worked out well the files U$~CHK1 and U$~CHK2 must be generated.
      UC checks for the existence of those files.

   When is it called?
      When an archive is converted, one of these batch files is used
      to extract the original archive. The extension of the archive
      corresponds with the xxx in the name of the batch file.

   Standard contents
      All batch files first add a file to an archive and then extract
      the entire archive. The main reason for this is improving
      reliability of the conversion, especially if certain tools are
      incompatible (e.g. older versions). If you are sure certain
      tools are present and up to date, you can simplify their batch
      files if you wish, to speed up conversion.

      U2_EXARC.BAT       First ARC is called.
                         When this fails, PK(X)ARC is called.
                         When this also fails PAK is called.

      U2_EXARJ.BAT       ARJ is called.

      U2_EXHA.BAT        HA (e.g. 0.982b) is called.

      U2_EXHPK.BAT       HPACK is called.

      U2_EXHYP.BAT       HYPER is called.

      U2_EXLZH.BAT       LHA is called.

      U2_EXPAK.BAT       PAK is called.

      U2_EXUCN.BAT       A .UC2  archive (being renamed to .UCN) is
                         extracted. NOTICE NOTHING IS DONE TO PRESERVE
                         FILES OF WHICH MULTIPLE VERSIONS ARE IN AN
                         ARCHIVE, ONLY THE LATEST VERSION IS EXTRACTED.

      U2_EXZIP.BAT       First PK(UN)ZIP 2.04ceg is called. When this is
                         not present PK(UN)ZIP 1.x is called. When this
                         fails, Info(UN)ZIP is called.

      U2_EXZOO.BAT       ZOO is called.

U2_XTRA.BAT
-----------
   Task
      Performs user defined operations during archive conversion.

   When is it called?
      When UC converts an archive, it first calls a U2_EX???.BAT file
      to extract all files from the original archive, the U2_EX???.BAT
      file then calls U2_XTRA.BAT when it has finished extracting all
      files from the archive.

   Standard contents
      No operations are performed. A disabled sample for adding
      banners to archives during conversion is included in
      U2_XTRA.BAT.


6.E OPTIMIZING PERFORMANCE.
===========================

In general UC will automatically utilize available resources (RAM,
microprocessor) in an optimal fashion. Please note UC does not stretch
beyond the limits of your system to achieve this. It only uses
officially documented methods to access XMS, EMS, DOS, Windows, OS/2
etc.. In many cases the methods UC uses have been double checked with
IBM, Microsoft, QuarterDeck, Novell and others. And of course
everything has been extensively tested on many different environments.

There are some tips to allow UC to work as fast as possible:

   - make as much base, EMS and XMS memory available as you can spare

   - (but) on systems supporting virtual memory (e.g. Windows NT, OS/2)
     you should not make TOO much memory available for UC (to prevent
     swapping)

   - select maximal speed in the configuration menu

   - or (e.g. if you prefer better compression)
      - enable advanced networking (when applicable)
      - enable EMS/XMS usage
      - enable 386/486/Pentium usage
      - set UC information to minimal

   - redirect the output of UC to the NUL device (e.g. UC X test > NUL)

   - install sufficient BUFFERS in your CONFIG.SYS and/or install a disk
     caching utility