Here are the messages printed via TapeMon by the BTN handler version 3.0,
in no particular order, with reasons for each message.

*** Sense: %s, other= %02X,%02X
       Printed when the tape drive returns a SCSI "check condition"
       in response to a SCSI command that BTN has sent to the drive.
       Sometimes this may indicate an error or problem, but not always.
       The reason for the condition is encoded into a "sense key"
       which is spelled out for you in this message.  The SCSI spec
       defines these keys:
          NO SENSE - nothing unusual to report
          RECOVERED ERROR - something went wrong, but the drive fixed it up
          NOT READY - human intervention is required (insert tape)
          MEDIUM ERROR - an unrecoverable flaw in the tape material
          HARDWARE ERROR - the drive is broken (still have your receipt?)
          ILLEGAL REQUEST - the SCSI command/function is not supported by
            this drive, or there are bits in the command that the drive
            doesn't like, or the drive is being asked to do something
            it doesn't feel like doing right now.
          UNIT ATTENTION - a transient condition generated whenever a
            new tape is inserted.
          DATA PROTECT - the tape medium is write protected
          BLANK CHECK - the drive has attempted to read past the blank spot,
            the end of the last-written file, or an erased tape.
          FILEMARK - the drive has attempted to read a filemark, which
            indicates the end of the file has been reached.
          END-OF-MEDIUM - the drive has reached physical end of the tape
          VOLUME OVERFLOW - some drives indicate this at end of tape
          INCORRECT LENGTH - BTN asked to read a block smaller than
            what was written on the tape.  BS is probably incorrect.

       The "other" bytes printed are bytes 12 and 13 of the sense data.
       For some drives, such as the MCD-40 and SCSI-2 drives, this is
       a subcode indicating more information about the sense key.

*** SCSI %s ERROR
       The scsi-direct driver/adapter returned an error in response to BTN's
       attempt to send a SCSI command to the drive.  These errors are
       defined by Commodore:
          SELF-UNIT - the UN number is the same as that of the SCSI adapter
          DMA - I don't know what this means.  Maybe an adapter problem.
          PHASE - the drive and the SCSI adapter are not in-sync with
             their SCSI phases.  There may be a mismatch in data transfer
             caused by incorrect block size (BS value), or the SCSI bus
             may be improperly terminated.
          PARITY - a parity error on the SCSI bus
          SELECT-TIMEOUT - the adapter timed out waiting for a response
             from the drive.

*** Can't get %u bytes for tape buffers
       There is insufficient memory to allocate two buffers of NB*BS
       bytes (or maybe the memory is too fragmented).  Use a smaller
       value for NB, or free up some memory, or reboot.

*** Invalid open name/combo %s
       * The name used to access the tape file is unrecognized.
          The name must be one of the following:  TAPE:  TAPE:R  TAPE:END
            TAPE:APP  TAPE:NR  TAPE:*  TAPE:number  TAPE:RAWCMD  TAPE:MODESEL
       * The function is incompatible with the open mode or drive model.
          Examples: you cannot read from TAPE:APP, and TAPE:APP is always
          invalid for direct access drives.

*** Current block size = %u
*** Mode Select, new block size %d
       Informative messages printed when the BS value is different than
       the block size of the drive.  BTN will attempt to command the
       drive to switch to the new size.

*** Capacity: %u blocks
       Informative message printed only for direct access drives describing
       the number of blocks available on this particular cartridge.

*** %s Opened file %d / at block %d
       Informative message printed when Open() is successful.

*** Closed at block %u, next file= %d
       Informative message printed when Close() is finished.
       The block number is the next available block.  The tape head
       is positioned ready to access this block for the next operation.
       The number of the file or block that will be written next is shown.

*** Function/mode error
       The application is attempting to mix Read()s and Write()s.
       It can't read while opened for writes, and vice versa.

*** %s is read-only
       The application is attempting to write to the device when
       the handler is operating in read only mode (RO-1).

*** %s is append-only
       The application is attempting to write over an existing file
       when the handler is operating in append-only mode (AO-1).

*** Disallowed seek type=%d off=%d curr=%d
       A Seek() request was rejected because the type of seek is not
       supported or it cannot be done at this point.

*** Error during read
*** Error during write
       Indicates that a medium error was encountered during a read or write.

*** Unsupported_Pkt=%d
       Informative message indicating that an AmigaDOS packet was
       rejected as "unknown", because the requested function does
       not apply to BTN.  Not usually a problem.

*** Skipping to end of data
*** (doing it the hard way)
       Informative message printed when Open()ing TAPE:APP.  If the
       drive doesn't directly support this function, the "hard way"
       message is printed, and BTN begins skipping individual files.

*** Skipping to file %d
       Informative message printed when reading from TAPE:number
       on a sequential drive.

*** Unable to position tape
       Printed when some kind of error occurs when BTN tries to get
       the tape into the necessary position for Open().  You will
       get a "replace volume" requester.

*** Time to insert tape# %d
       Informative message printed at end of tape.  Also a requester.

*** Writing block %u x %d
*** Reading block %u x %d
       Informative messages printed just before a SCSI read or write
       command is sent to the drive.  The block number is relative
       to the beginning of the file for sequential drives, and is
       the actual block number for direct access drives.  The length
       is the number of bytes (NB*BS).

*** Rewinding
       You guess this one...

*** Writing filemark
       Informative message printed when Close()ing a file being written.

*** Retensioning
       Informative message printed when Unit Attention status occurs and
       RT-1 was specified in the mountlist.  The retensioning operation
       may take several minutes to complete.

*** Raw command %02X
       Informative message printed when writing to TAPE:RAWCMD.

*** User Mode-Select
       Informative message printed when writing to TAPE:MODESEL.