ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                            º
º                ECRLINK v1.10 beta test                     º
º                                                            º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    The EcrLink system has been designed to upload the
programming and sales information from certain models of SHARP
cash registers, save this information on disk and download to the
cash register again if required. 

    Anyone who has had the misfortune to lose this information
and has spent, up to a few weeks in some cases, time restoring
this information, will, I'm sure, appreciate this system. You do
not need any fancy boards installed in your register as the
system works through the service port built into these machines,
usually used for transferring from one register to another.

    It would be nice to be able to write that this program can
be used with any of the Sharp models but, unfortunately, Sharp
has changed the comms protocols on some ranges and is reluctant
to release the information as if it is some great secret.

    Anyhow, this program has been tested on desktop and laptop
machines, from XT's to 486's ( 286 or better recommended ) and 
seems to work OK. Cash registers tested are the ER-3100, ER-3110 
and the ER-2910, others with the same protocol should work OK.

    At the moment, a RS-232C level convertor, the ER-52LC, ER-67LC 
or equivalent is required because of the different voltage levels
on the PC and Register serial ports. I would like to incorporate
a level convertor in the actual transfer cable, probably powered
by the PC's port and I would appreciate any info on designing this.

    The special cable with the correct DIN type plug for connecting
to the register comes complete with the level convertor.


                 PC to ECR level convertor cable

              PC 9-Pin           ER-52LC/67LC 25-Pin

         25-Pin in brackets      


         TX    3 (2) þÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄþ 3   RD
                                             
         RX    2 (3) þÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄþ 2   SD
                                              
         CTS   8 (5) þÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄþ 20   ER
                               ³                  
         DSR   6 (6) þÄÄÄÄÄÄÄÄÄÙ         
                                    
         SG    5 (7) þÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄþ 7  GND 
                                              
         DTR   4 (20) þÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄþ 5   CS
                               ³          
                               ÃÄÄÄÄÄÄÄÄÄÄþ 6   DR 
                               ³          
                               ÀÄÄÄÄÄÄÄÄÄÄþ 8   CD


    I would also be most grateful to get hold of upload/download
protocol for the ER-4100 and ER-4110 as these are popular units,
with large memories, but whose port handshaking is different. 

    Please send your comments and/or suggestions as to how you
find the system, improvements that could be made etc. to any of
the addresses below. 


    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
    º  Phil Webb                                       º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
    º  P.O. Box 34349, Jeppestown,                     º
    º  2043, Republic of South Africa                  º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
    º  Beltel Mail Number: 802240                      º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶ 
    º  Internet Email: phil.webb@vcbbs.proxima.alt.za  º
    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼