Memory Manager Example Settings:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

**********************************************************************
IMPORTANT NOTE!

These are only EXAMPLE configurations for these Memory Managers.  ALL
Memory Manager switches are HARDWARE DEPENDENT.  Your settings will
most likely differ from those shown below.

If you are unsure of the settings you should use, run the appropriate
configuration program for your memory manager.

              Memory Mgr.        Configure with
              ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                QEMM             OPTIMIZE
                386MAX           MAXIMIZE
                MS DOS 6         MEMMAKER
                PC DOS 6         RAMSETUP


**********************************************************************

MS DOS 6 / EMM386 - CONFIG.SYS

DEVICE=C:\DOS\HIMEM.SYS
DEVICE=C:\DOS\EMM386.EXE RAM HIGHSCAN X=D000-D1FF
BUFFERS=15,0
FILES=60
DOS=UMB
LASTDRIVE=E
FCBS=4,0
DEVICE = C:\hyp\hyperdkx.EXE c:1024 cw:1024 h v
DEVICEHIGH /L:1,12048 =C:\DOS\SETVER.EXE
DOS=HIGH
SHELL=C:\DOS\COMMAND.COM C:\DOS\  /p

*Alternate EMM386 CONFIG.SYS settings under DOS 6
DEVICE=C:\DOS\EMM386.EXE noems X=D000-D1FF


MS DOS 6 / EMM386 - AUTOEXEC.BAT

@ECHO OFF
PROMPT $p$g
PATH C:\DOS;c:\clarion3;c:\cmd;c:\norton
loadhigh doskey
SET TEMP=C:\DOS

----------------------------------------------------------------------

PC DOS 6.1 / EMM386 - CONFIG.SYS

***** NOTE: If you do not have the most recent version of IBM DOS 6
you may have problems running CDD.  The fix for IBMDOS.COM is on the
latest disk compression diskette (if your version did not come w/ disk
compression) or available for download from the Clarion Forum on
CompuServe (Go Clarion) in Library 8.


DEVICE=C:\DOS\HIMEM.SYS
DEVICE=C:\DOS\EMM386.EXE NOEMS RAM X=A000-B1FF I=B200-B7FF X=B800-C7FF I=C800-CFFF X=D000-D3FF I=D400-EFFF X=F000-F7FF H=64 A=7 D=32
DEVICE=C:\DOS\RAMBOOST.EXE LOAD
DOS=HIGH
DEVICE=C:\DOS\SETVER.EXE
FILES=50
BUFFERS=20
DEVICE=C:\HYPERDKX.EXE C:640 CW:512 H OR
SHELL=C:\DOS\COMMAND.COM C:\DOS\  /p
STACKS=0,0


PC DOS 6.1 / EMM386 - AUTOEXEC.BAT


@ECHO OFF
SET CLATMP=C:\TEMP
SET TEMP=C:\TEMP
SET IBMAV=C:\DOS
CALL C:\DOS\IBMAVDR.BAT C:\DOS\
PROMPT $_$t$_$p$g
PATH C:\DOS;C:\;C:\CMD;C:\CLARION3;C:\CDDW\BIN;C:\NU;C:\CLARION;C:\WINDOWS
Rem --- Check for lost clusters or chains
CHKDSK /F
Rem --- Delete any Temp Files left over
DEL C:\TEMP\*.$$$
Rem --- Load Doskey
C:\DOS\DOSKEY
Rem --- Load Mouse
C:\DOS\MOUSE
Rem --- Load Network Drivers
IPX
NET5.COM


----------------------------------------------------------------------

MS DOS 5 / EMM386 - CONFIG.SYS

DEVICE=C:\DOS\HIMEM.SYS
DEVICE=C:\DOS\EMM386.EXE NOEMS I=E000-EFFF
DOS=HIGH,UMB
SHELL=C:\DOS\COMMAND.COM C:\DOS\ /P /E:186
FILES=50
BUFFERS=5
STACKS=0,0
BREAK=ON

Note : Address location E000-EFFF is machine dependent.  This memory
       location may increase your conventional memory by +30K.


MS DOS 5 / EMM386 - AUTOEXEC.BAT

PROMPT $p$g
PATH C:\;C:\CLARION3;C:\DOS
Rem
Rem  In the next statement AUTO switch enables protected mode access
Rem
EMM386 AUTO
LH BTRIEVE /E /M:48 /P:4096 /T:\CLARION3\CLARION.TRN
LH MOUSE
LH DOSKEY

----------------------------------------------------------------------

386/MAX - CONFIG.SYS

DOS=HIGH
FILES=50
         Several CONFIG.SYS variations:

DEVICE=C:\386max\386max.sys pro=c:\386max\386max.pro
DEVICE=C:\386max\386max.sys pro=c:\386max\386max.pro NODPMI
DEVICE=C:\386MAX\386load.sys size=12576 flexframe prog=C:\HYPERKEY.EXE
DEVICE=C:\386MAX\386load.sys size=45360 flexframe prog=C:\HYPERDKX.EXE C:1024 H
DEVICE=C:\386MAX\386load.sys size=9040 flexframe prog=C:\DOS\ANSI.SYS
SHELL=C:\DOS\COMMAND.COM C:\DOS\ /E:186 /p
STACKS=0,0

386/MAX - AUTOEXEC.BAT

PROMPT = $P$G
PATH C:\;C:\CLARION3;C:\DOS
C:\386MAX\386load size=6400 flexframe prog=DOSKEY
C:\386MAX\386load size=10736 prgreg=2 flexframe prog=MOUSE /2

----------------------------------------------------------------------

QEMM386 - CONFIG.SYS

DEVICE=C:\QEMM\QEMM386.SYS R:5 X=B000-B0FF X=C600-C7FF DBF=2 ST:M RAM
DOS=HIGH
DEVICE=C:\QEMM\LOADHI.SYS /R:2 C:\DOS\ANSI.SYS
DEVICE=C:\QEMM\LOADHI.SYS /R:1 C:\MOUSE.SYS
SHELL=C:\DOS\COMMAND.COM /E:500 /P
BUFFERS=20
FILES=70

QEMM386 - AUTOEXEC.BAT

PROMPT $P$G
PATH  C:\;C:\CLARION3;C:\DOS;C:\QEMM
C:\QEMM\LOADHI /R:3 /RES=4336 /SQT=D000-D0FF \DOS\DOSKEY
C:\QEMM\LOADHI /R:2 LSL
C:\QEMM\LOADHI /R:4 TRXNET
C:\QEMM\LOADHI /R:2 /RES=16096 /SQT=C600-C7FF IPXODI
C:\QEMM\LOADHI /R:4 NETX

QEMM386 - CONFIG.SYS

DEVICE=C:\QEMM\QEMM386.SYS R:5 X=B000-B0FF X=C600-C7FF DBF=2 ST:M RAM
DOS=HIGH
DEVICE=C:\QEMM\LOADHI.SYS /R:2 C:\DOS\ANSI.SYS
DEVICE=C:\QEMM\LOADHI.SYS /R:1 C:\MOUSE.SYS
SHELL=C:\DOS\COMMAND.COM /E:500 /P
BUFFERS=20
FILES=70