SHADOW RAM MEMORY CONTROLLERS

                                  supported by


                        THE LAST BYTE MEMORY MANAGER (tm)







                                  Version 2.41










                              Copyright (C) 1990-94
                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                        Menlo Park, California 94025-1802
                                  415-364-9847














        The Last Byte Memory Manager is a trademark of Key Software Products.



        



                                TABLE OF CONTENTS



        CHAPTER 1 - INTRODUCTION        ...........................    1
           1.1  Hardware Requirements       .......................    1
           1.2  Checking Compatibility Using CHIPSET     ..........    1
           1.3  Supported Chipsets       ..........................    2
              1.3.1  ACC Microelectronics       ...................    2
              1.3.2  Acer Laboratories Incorporated (ALI)     .....    2
              1.3.3  AddTech Research (PCChip)      ...............    3
              1.3.4  Appian Technology       ......................    3
              1.3.5  Atmel Corporation       ......................    4
              1.3.6  Biostar Systems (BIOTEQ)      ................    4
              1.3.7  Chips and Technologies      ..................    4
              1.3.8  EFAR Microelectronics       ..................    5
              1.3.9  ETEQ Microelectronics       ..................    5
              1.3.10  Forex Computer Corporation      .............    6
              1.3.11  Headland Technology (G2)      ...............    6
              1.3.12  Hedaka        ...............................    7
              1.3.13  HINT Corporation       ......................    7
              1.3.14  Intel Corporation       .....................    7
              1.3.15  Macronix Incorporated (MX)      .............    8
              1.3.16  Micro Integration Corporation (MIC)     .....    8
              1.3.17  Mosel Corporation       .....................    8
              1.3.18  Oak Technology       ........................    8
              1.3.19  OPTi Electronics       ......................    9
              1.3.20  PC Chip       ...............................   10
              1.3.21  PicoPower Technology       ..................   10
              1.3.22  Silicon Integrated Systems (SiS)     ........   10
              1.3.23  Sun Electronics (SUNTAC)      ...............   11
              1.3.24  Symphony Laboratories       .................   11
              1.3.25  Texas Instruments (TI)      .................   11
              1.3.26  UNIchip Incorporated       ..................   12
              1.3.27  United Microelectronics Corporation (UMC)       12
              1.3.28  VIA Technologies       ......................   13
              1.3.29  Victronix Technology       ..................   13
              1.3.30  VLSI Technology       .......................   13
           1.4  Unsupported Chipsets       ........................   14
              1.4.1  No Shadow Ram Support     ....................   14
              1.4.2  Shadow Ram is not Read/Write    ..............   14
              1.4.3  Overly Complex Control      ..................   15
              1.4.4  Locked Configuration Registers      ..........   15
              1.4.5  Configuration I/O Ports Reassigned     .......   15













        




        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 1


                        CHAPTER 1 - INTRODUCTION        


        1.1 Hardware Requirements        

        To  install The Last Byte Memory Manager, your computer must have
        a  means  of providing read-write memory in the Upper Memory Area
        between  640k  and  1 megabyte.  This is possible if you have any
        of the following, listed in order of preference: 

             o  One  of  the  shadow  ram  memory  controller  chips
                listed in this document, or 

             o  An  expanded memory board (EEMS, LIM 3.2 EMS, or LIM
                4.0 EMS), or 

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ NOTE: Using a LIM 3.2 EMS board is not advised  ³ 
                ³ as a method of providing upper memory.  It pro- ³ 
                ³ vides only 64k of upper memory and prevents ap- ³ 
                ³ plication software from using expanded memory.  ³ 
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

             o  Fixed  RAM memory already resident in the upper area
                (such  as  the 32-bit "Built In Memory" installed in
                some Compaq 386 machines), or 

             o  A  386sx,  386,  486,  or  486sx  processor  and the
                Microsoft  Windows  3.0/3.1  or  DOS  5  versions of
                EMM386.  



        1.2 Checking Compatibility Using CHIPSET      

        CHIPSET  is a program that attempts to determine if your computer
        has  one  of the memory controllers required to use The Last Byte
        Memory  Manager.   To  run  CHIPSET, simply enter its name on the
        command line: 

                A>CHIPSET 

        and  follow  the  prompts.   CHIPSET  will  try  to  identify the
        particular  memory controller you have, if any.  If it can't find
        a  memory  controller, it will look for fixed memory in the upper
        area  or  expanded  memory as a means of installing The Last Byte
        Memory  Manager.   If  it  is  successful,  it  will give you the
        option  of  automatically linking to the INSTALL program to setup
        for use of The Last Byte Memory Manager.  

        CHIPSET   automatically  senses  whether  you  have  a  color  or



        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 2


        monochrome  display  to  determine  how  to  present  data on the
        screen.   However,  you  may  force  the mode by using one of the
        command  line  options:  /MONO  or  /COLOR (for monochrome liquid
        crystal displays).  

        If  your  computer  has  one of the listed devices, then The Last
        Byte Memory Manager should work on your computer.  


        1.3 Supported Chipsets        

        Key  Software  Products  is  continually  adding  support for new
        chipsets  as  they  become  known to us and technical information
        can  be  obtained.  Those that are currently supported in version
        2.41  are  listed in the paragraphs below.  Some that we know of,
        but  which  cannot  be  supported are listed near the end of this
        document.  

        In  what  follows,  you will occassionally see "+32k" appended to
        the  end  of  the  total  amount  of  shadow  ram indicated for a
        particular  chipset.   This means that there is additional shadow
        ram  in  the F000-FFFF region, but that it is read-only; however,
        if  you  have a VGA or EGA adapter and a "split" bios, you may be
        able  to  gain  up to an additional 32k by using the MOVE=OVERLAY
        option of LASTBYTE.SYS.  

        An  adapter card (like some disk controllers) that uses a portion
        of  the  upper  memory address space usually requires that shadow
        ram  in  the  same address space be disabled.  Thus shadow ram is
        usually  organized into segments that can be individually enabled
        or  disabled.   Even  though  an  adapter  may  only  use a small
        portion  of  one  shadow  ram segment, the entire segment must be
        disabled.   How this affects your system can be determined by the
        information under the columns labelled "Organization".  


        1.3.1 ACC Microelectronics        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        ACC2036         64k             Page Frame      4x16k
        ACC2121         64k             Page Frame      4x16k
        ACC2300         128k            E0000-FFFFF     1x128k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        ACC2036         Single Chip Solution for the 286 and 386SX
        ACC2121         Turbo PC/AT Chip Set for the 286 and 386SX
        ACC2300         82300 386 AT Chip Set





        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 3


        1.3.2 Acer Laboratories Incorporated (ALI)      

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        M1207           384k            A0000-FFFFF     6x64k
        M1209           128k            E0000-FFFFF     1x128k
        M1217           256k            C0000-FFFFF     8x32k
        M1219           256k            C0000-FFFFF     8x32k
        M1409           256k            C0000-FFFFF     16x16k
        M1419           256k            C0000-FFFFF     8x32k
        M1429           256k            C0000-FFFFF     8x32k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        M1207           80286 Single Chip
        M1209           80386SX PC/AT Super-Integration Chip
        M1217           80386SX Single Chip
        M1219           80486SX/80486DX Single Chip
        M1409           80486SX/80486DX Single Chip
        M1419           ISA 486/386 Cache System Chipset
        M1429           486DX/P24T VESA Single-Chip


        1.3.3 AddTech Research (PCChip)       

        AddTech  chipsets  are  usually  labelled  "PCChip"  or "Hedaka".
        AddTech  designs  their  chips for use on their own motherboards,
        and   they  identify  their  chipsets  by  the  motherboard  part
        numbers.   There  is at least one AddTech chipset that is used on
        two   different  motherboards  with  different  motherboard  part
        numbers.   To  avoid  confusion,  The  Last  Byte  Memory Manager
        refers  to  these  chips  using  "PCCHIP"  followed  by  a unique
        number.  

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        PCCHIP1         256k            C0000-FFFFF     16x16k
        PCCHIP2         192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        PCCHIP1         Used on 286/386SX AT motherboards M205 and M209
        PCCHIP2         Used on 386 AT motherboard M321


        1.3.4 Appian Technology        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        P915            256k            C0000-FFFFF     16x16k




        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 4


        Part Number     Manufacturer's Description
        -----------     --------------------------
        P915            486/386DX System Controller


        1.3.5 Atmel Corporation        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        AT40281         192k+32k        C0000-EFFFF     12x16k
        AT40283         192k+32k        C0000-EFFFF     12x16k
        AT40391         192k+32k        C0000-EFFFF     12x16k
        AT40493         192k+32k        C0000-EFFFF     12x16k
        AT40495         192k+32k        C0000-EFFFF     12x16k
        AT40498         192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        AT40281         386SX Core Logic Controller w/Cache
        AT40283         386SX Core Logic Controller w/o Cache
        AT40391         80386DX PC/AT Chip Set
        AT40493         80486DX PC/AT Chip Set
        AT40495         80486SX PC/AT Chip Set
        AT40498         80486 Core Logic Controller


        1.3.6 Biostar Systems (BIOTEQ)       

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        82C3480         256k            C0000-FFFFF     8x32k
        82C3491         256k            C0000-FFFFF     8x16k+2x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        82C3480         ISA 486/386 Cache System Chipset
        82C3491         ISA 486/386 Single Chip


        1.3.7 Chips and Technologies       

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        82C100          64k             Page Frame      4x16k
        82C212          384k            A0000-FFFFF     24x16k
        82C222          384k            A0000-FFFFF     24x16k
        82C230          384k            A0000-FFFFF     24x16k
        82C235          384k            A0000-FFFFF     24x16k
        82C241          384k            A0000-FFFFF     24x16k
        82C302          384k            A0000-FFFFF     24x16k
        82C307          384k            A0000-FFFFF     24x16k



        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 5


        82C311          384k            A0000-FFFFF     24x16k
        82C322          384k            A0000-FFFFF     16x16k+1x128k
        82C351          384k            A0000-FFFFF     24x16k
        82C812          384k            A0000-FFFFF     24x16k
        82C836          384k            A0000-FFFFF     24x16k
        82C841          384k            A0000-FFFFF     24x16k
        84021           384k            A0000-FFFFF     2x64k+4x16k+3x64k
        84031           384k            A0000-FFFFF     2x64k+4x16k+3x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        82C100          IBM PS/2-30 and Super XT Compatible chip
        82C212          CS8221 NEAT (tm) chipset
        82C222          CHIPS/250 PS/2 50/60 chipset
        82C230          PS/2 30 Single Chip Controller
        82C235          SCAT (tm) Single Chip AT VLSI chip
        82C241          CS8223 LeAPset (tm) chipset
        82C302          CS8230 386/AT CHIPSet (tm)
        82C307          CS8231 386/AT CHIPSet (tm)
        82C311          CS8233 PEAK 386/AT CHIPSet (tm)
        82C322          CHIPS/280 PS/2 70/80 chipset
        82C351          CS82310 PEAK DM/386 AT CHIPSet (tm)
        82C812          CS8281 NEATsx (tm) chipset
        82C836          SCATsx (tm) Single Chip AT VLSI chip
        82C841          CS8283 LeAPset-sx (tm) chipset
        84021           ISA/486 chipset
        84031           ISA/486 chipset

        The  84021  provides  up  to 384k of memory, but any of the first
        two  and  last  two  64k blocks might be "locked" and unavailable
        due  to  the design of your particular bios.  This may reduce the
        amount of memory from 384k to as little as 128k.  


        1.3.8 EFAR Microelectronics        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        82EC495         192k+32k        C0000-EFFFF     12x16k
        82EC798         192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        82EC495         EF8290WB 486/386 PC/AT ChipSet
        82EC798         EC798 386/486 PC/AT Single Chip









        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 6


        1.3.9 ETEQ Microelectronics        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        ET6000          192k+32k        C0000-EFFFF     3x64k
        ET82C390SX      192k+32k        C0000-EFFFF     12x16k
        ET82C391        192k+32k        C0000-EFFFF     12x16k
        ET82C491        192k+32k        C0000-EFFFF     12x16k
        ET82C4901       192k+32k        C0000-EFFFF     12x16k
        ET9000          192k+32k        C0000-EFFFF     3x64k
        ET9800/ET391SX  192k+32k        C0000-EFFFF     3x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        ET6000          Cheetah 486DX/SX Non-Cache System
        ET82C390SX      Panda 386SX Single Chip w/Direct Mapped Cache
        ET82C391        Bobcat 386DX/486DX chipset
        ET82C491        Cougar 386DX/486DX chipset
        ET82C4901       Bengal 386DX/486DX chipset
        ET9000          Jaguar 486DX/SX Cache System
        ET9800/ET391SX  Firefox 386SX Write Back chipset

        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³ If you have a ET9800/ET391SX chipset and an     ³ 
        ³ adapter that occupies non-shadow ram address    ³
        ³ space between C8000-CFFFF, you will need to re- ³ 
        ³ configure that adapter to use another location. ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        The  CHIPSET  program cannot distinguish between the ET82C391 and
        ET82C491.  


        1.3.10 Forex Computer Corporation       

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        FRX36C300       256k            C0000-FFFFF     6x32k+1x64k
        FRX46C411       256k            C0000-FFFFF     6x32k+1x64k
        FRX46C421       256k            C0000-FFFFF     6x32k+1x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        FRX36C300       FRX36C300/200 Cache chipset
        FRX46C411       FRX46C411/412 Cache chipset
        FRX46C421       FRX46C421/422 Cache chipset








        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 7


        1.3.11 Headland Technology (G2)       

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        HT12            64k             Page Frame      4x16k
        HT18            128k            C0000-DFFFF     8x16k
        HT21            128k            C0000-DFFFF     8x16k
        HT22            128k            C0000-DFFFF     8x16k
        HT103           128k            C0000-DFFFF     8x16k
        HT113           128k            C0000-DFFFF     8x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        HT12            Single 286 AT Chip
        HT18            286/386SX Advanced Memory Manager Chip
        HT21            286/386SX Advanced Memory Manager Chip
        HT22            286/386SX Advanced Memory Manager Chip
        HT103           286/386SX Advanced Memory Manager Chip
        HT113           286/386SX Advanced Memory Manager Chip

        The  CHIPSET  program  cannot  distinguish  between  the HT18 and
        HT22.  


        1.3.12 Hedaka         

        See section on AddTech Research.  


        1.3.13 HINT Corporation        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        HINT8001        256k            C0000-FFFFF     4x32k+2x64k
        HINT8005        256k            C0000-FFFFF     4x32k+2x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        HINT8001        Caesar Super ISA chipset
        HINT8005        VLISA Single Chip 


        1.3.14 Intel Corporation        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        82343           192k+32k        C0000-EFFFF     12x16k
        82346           192k+32k        C0000-EFFFF     12x16k
        82359           384k            A0000-FFFFF     24x16k





        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 8


        Part Number     Manufacturer's Description
        -----------     --------------------------
        82343           82340SX Chip Set
        82346           82340DX Chip Set
        82359           82350DT EISA Chip Set


        1.3.15 Macronix Incorporated (MX)       

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        MX83C305        256k            C0000-FFFFF     6x32k+1x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        MX83C305        Compactest 386DX Chipset with Cache


        1.3.16 Micro Integration Corporation (MIC)      

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        MIC9283         192k+32k        C0000-EFFFF     12x16k
        MIC9382         192k+32k        C0000-EFFFF     12x16k
        MIC9391         192k+32k        C0000-EFFFF     12x16k
        MIC9498         192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        MIC9283         386SX PC/AT Single Chip w/Posted Write or Write-Thru
        MIC9382         386DX PC/AT Chip Set w/Write-Thru Cache
        MIC9391         386DX PC/AT Chip Set w/Write-Back Cache
        MIC9498         486DX PC/AT Single Chip w/Write-Back Cache


        1.3.17 Mosel Corporation        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        MS400           256k            C0000-FFFFF     4x16k+3x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        MS400           486SX/DX Single Chip AT


        1.3.18 Oak Technology        







        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                 9


        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        OTI-021         256k            C0000-FFFFF     4x32k+2x64k
        OTI-041         256k            C0000-FFFFF     4x32k+2x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        OTI-021         OTI-020 Desktop PC Chip Set
        OTI-041         OTI-040 OakNote Chip Set

        The  CHIPSET  program  cannot distinguish between the OTI-021 and
        OTI-041.  


        1.3.19 OPTi Electronics        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        82C281          192k+32k        C0000-EFFFF     12x16k
        82C282          192k+32k        C0000-EFFFF     12x16k
        82C283          192k+32k        C0000-EFFFF     12x16k
        82C291          256k            C0000-FFFFF     12x16k+1x64k
        82C295          256k            C0000-FFFFF     12x16k+1x64k
        82C382          192k+32k        C0000-EFFFF     12x16k
        82C391          192k+32k        C0000-EFFFF     12x16k
        82C461          192k+32k        C0000-EFFFF     12x16k
        82C463          192k+32k        C0000-EFFFF     12x16k
        82C482          192k+32k        C0000-EFFFF     12x16k
        82C491          192k+32k        C0000-EFFFF     12x16k
        82C493          192k+32k        C0000-EFFFF     12x16k
        82C495          192k+32k        C0000-EFFFF     12x16k
        82C495SLC       192k+32k        C0000-EFFFF     12x16k
        82C495SX        192k+32k        C0000-EFFFF     12x16k
        82C496A         192k+32k        C0000-EFFFF     12x16k
        82C496B         256k            C0000-FFFFF     12x16k+1x64k
        82C498          192k+32k        C0000-EFFFF     12x16k
        82C499          192k+32k        C0000-EFFFF     12x16k
        82C597          256k            C0000-FFFFF     8x16k+2x64k
        82C682          256k            C0000-FFFFF     8x16k+2x64k
        82C683          256k            C0000-FFFFF     8x16k+2x64k
        82C801          192k+32k        C0000-EFFFF     12x16k
        82C802          192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        82C281          Cache SX/AT chipset
        82C282          Non-Cache SX/AT chipset
        82C283          Block Interleave SX/AT chipset
        82C291          SXWB PC/AT chipset
        82C295          SLCWB PC/AT chipset
        82C382          HiD/386 AT chipset



        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                10


        82C391          386WB PC/AT chipset
        82C461          Notebook PC/AT chipset
        82C463          SCNB Single Chip Notebook chipset
        82C482          HiB/486 AT chipset
        82C491          486SXWB PC/AT chipset
        82C493          486SXWB PC/AT chipset
        82C495          486SXWB PC/AT chipset
        82C495SLC       495SLC PC/AT chipset
        82C495SX        LCWB PC/AT chipset
        82C496A         DXBB PC/AT chipset (Rev. A)
        82C496B         DXBB PC/AT chipset (Rev. B)
        82C498          DXWB PC/AT chipset
        82C499          DXSC PC/AT Single Chip
        82C597          PTMA WB-V PC/AT chipset
        82C682          386/486WB EISA chipset
        82C683          386/486AWB EISA chipset
        82C801          SCWB2 PC/AT Single Chip
        82C802          SCWB2 PC/AT Single Chip

        The  CHIPSET  program  cannot  distinguish between the 82C281 and
        82C282,  or  among the 82C491, 82C493, and 82C495, or between the
        82C291 and 82C295.  


        1.3.20 PC Chip        

        See section on AddTech Research.  


        1.3.21 PicoPower Technology        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        PT86C168        256k            C0000-FFFFF     12x16k+1x64k
        PT86C268        256k            C0000-FFFFF     12x16k+1x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        PT86C168        Evergreen Portable Computer Core Logic Chip
        PT86C268        Evergreen HV Core Logic Chip (Hybrid 3.3v/5.0v)


        1.3.22 Silicon Integrated Systems (SiS)      

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        85C360          256k            C0000-FFFFF     6x32k+1x64k
        85C401          256k            C0000-FFFFF     6x32k+1x64k
        85C411          256k            C0000-FFFFF     6x32k+1x64k
        85C460          256k            C0000-FFFFF     6x32k+1x64k
        85C461          256k            C0000-FFFFF     6x32k+1x64k



        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                11


        85C471          256k            C0000-FFFFF     6x32k+1x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        85C360          ISA 386DX Single Chip
        85C401          ISA 486DX/SX Chipset
        85C411          EISA 386/486 Chipset
        85C460          ISA 486DX/SX Single Chip
        85C461          ISA 486DX/SX Single Chip
        85C471          Green PC ISA-VESA Single Chip

        The  CHIPSET  program  cannot  distinguish between the 85C460 and
        85C461.  


        1.3.23 Sun Electronics (SUNTAC)       

        All  SunTac  chips  provide  128k  of  memory  in four 32k blocks
        between  E0000-FFFFF.   An  additional  128k  in eight 16k blocks
        between  C0000-DFFFF  is available at the expense of all Expanded
        Memory  by adding the word NOEMS to the SUNTAC Physical option as
        in: Physical=ST62C202,NOEMS.  

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        ST62C202        128k/256k       C0000-FFFFF     [8x16k]+4x32k
        ST62C241        128k/256k       C0000-FFFFF     [8x16k]+4x32k
        ST62C251        128k/256k       C0000-FFFFF     [8x16k]+4x32k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        ST62C202        Chipset 20 for 286
        ST62C241        Chipset 24 for 386
        ST62C251        Chipset 25 for 286 and 386sx


        1.3.24 Symphony Laboratories        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        SL82C361        256k            C0000-FFFFF     8x16k+2x64k
        SL82C461        256k            C0000-FFFFF     8x16k+2x64k
        SL82C471        256k            C0000-FFFFF     8x16k+2x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        SL82C361        Haydn SL82C360 80386DX/SX chipset
        SL82C461        Haydn SL82C460 80486 chipset
        SL82C471        Mozart SL82C470 486/386 EISA chipset





        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                12


        1.3.25 Texas Instruments (TI)       

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        TACT82411       384k            A0000-FFFFF     24x16k
        TACT82S411      384k            A0000-FFFFF     24x16k
        TACT83442       256k            C0000-FFFFF     16x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        TACT82411       Snake Single-Chip AT Controller
        TACT82S411      Snake+ Single-Chip AT Controller
        TACT83442       Tiger TACT83000 AT Chip Set

        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³ The TACT83442 can only be supported if the main ³ 
        ³ bios has not reassigned the I/O ports that are  ³
        ³ used to access the configuration registers from ³ 
        ³ their default values.                           ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 


        1.3.26 UNIchip Incorporated        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        U4800           192k+32k        C0000-EFFFF     3x64k
        U4800VLX        192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        U4800           386/486 AT Chip Set
        U4800VLX        386/486 AT Chip Set


        1.3.27 United Microelectronics Corporation (UMC)      

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        UM82C212        384k            A0000-FFFFF     24x16k
        UM82C391        256k            C0000-FFFFF     8x16k+2x64k
        UM82C481        256k            C0000-FFFFF     8x16k+2x64k
        UM82C491        256k            C0000-FFFFF     8x16k+2x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        UM82C212        UM82C210 386SX/286 AT Chip Set
        UM82C391        UM82C390 40Mhz 80386 Chip Set
        UM82C481        UM82C480 50Mhz 80486 Chip Set
        UM82C491        UM82C491 386/486 Single Chip




        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                13



        1.3.28 VIA Technologies        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        VT82C470        256k            C0000-FFFFF     8x16k+2x64k
        VT82C475        256k            C0000-FFFFF     8x16k+2x64k
        VT82C495        256k            C0000-FFFFF     8x16k+2x64k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        VT82C470 - From the Jupiter Chip Set (w/o cache)
        VT82C475 - From the Jupiter Chip Set (w/cache)
        VT82C495 - From the Venus Chip Set


        1.3.29 Victronix Technology        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        VIC92C4800      192k+32k        C0000-EFFFF     12x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        VIC92C4800      486DX/SX ISA PC/AT Non-Cache Single Chip


        1.3.30 VLSI Technology        

        Part Number     Shadow Ram      Address Range   Organization
        -----------     ----------      -------------   ------------
        VL82C202        384k            A0000-FFFFF     6x64k
        VL82C310        384k            A0000-FFFFF     4x32k+8x16k+4x32k
        VL82C311        384k            A0000-FFFFF     4x32k+8x16k+4x32k
        VL82C315        384k            A0000-FFFFF     4x32k+8x16k+4x32k
        VL82C316        384k            A0000-FFFFF     4x32k+8x16k+4x32k
        VL82C320        192k+32k        C0000-EFFFF     12x16k
        VL82C330        192k+32k        C0000-EFFFF     12x16k
        VL82C480        384k            A0000-FFFFF     24x16k
        VL82C481        384k            A0000-FFFFF     24x16k
        VL82C486        384k            A0000-FFFFF     24x16k

        Part Number     Manufacturer's Description
        -----------     --------------------------
        VL82C202        PC/AT-Compatible High Speed Memory Controller
        VL82C310        SCAMP 286/386sx Chip Set
        VL82C311        SCAMP 286/386sx Chip Set
        VL82C315        SCAMP II PC/AT-Compatible System Controller
        VL82C316        SCAMP II Chip Set for Power-Managed Portables
        VL82C320        TOPCAT 286/386sx Chip Set
        VL82C330        TOPCAT 386 DX Chip Set



        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                14


        VL82C480        486 System/Cache/ISA Bus Controller
        VL82C481        486 System/Cache/ISA Bus Controller
        VL82C486        Single Chip, High Performance 486 PC/AT Controller

        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³ Pin 69 on th VL82C202 controls whether its      ³ 
        ³ shadow ram is enabled or relocated.  This pin   ³
        ³ is usually tied to a jumper on the motherboard  ³ 
        ³ which must be set properly to work.             ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        The  CHIPSET  program cannot distinguish between the VL82C315 and
        VL82C316.  


        1.4 Unsupported Chipsets        

        If  your computer has shadow ram capability, then it probably has
        a  shadow ram memory controller.  However, some of these chipsets
        cannot  be  supported by The Last Byte Memory Manager for reasons
        shown below.  

        Some  of  these  chips, however, do have hardware EMS support and
        thus  many  of  their motherboards come with an EMS device driver
        designed  specifically  to take advantage of this capability.  So
        in  many  cases,  you can install this driver first, and then The
        Last  Byte  Memory  Manager can use it to manage the upper memory
        area.  


        1.4.1 No Shadow Ram Support      

        Some   of   the   older   chipsets  do  not  provide  shadow  ram
        capability.  

        Examples: Western Digital chipsets
                  Texas Instruments TACT82300 series
                  Early Suntac chipsets (ST62BC001-6)
                  United Microelectronics Corp. UM82C231


        1.4.2 Shadow Ram is not Read/Write     

        Some  chipsets  have  shadow ram, but can only put it into either
        write-only  mode  (for copying rom contents to ram), or read-only
        mode  (to  prevent accidental writes into what's supposed to be a
        copy  of  rom).  The hardware EMS in some such chipsets sometimes
        provides  a limited amount (e.g., 64k) of Hi-DOS memory, but only
        if the user doesn't need expanded memory.  

        Examples: CONTAQ 82C591 (no hardware EMS support)



        Copyright (C) 1990-94, Key Software Products. All Rights Reserved



        Jun 09, 1994      SHADOW RAM MEMORY CONTROLLERS                15


                  Headland/G2 (many do have hardware EMS however)
                  ACC Microelectronics (many do have hardware EMS)
                  USA Integration (USAi) (no hardware EMS)


        1.4.3 Overly Complex Control       

        The  Last Byte Memory Manager software is table-driven, making it
        relatively   easy   to   adapt  to  different  memory  controller
        architectures, but there are limits!   

        Examples: Zymos/Appian System 90 chipset
                  United Microelectronics Corp UM82C384, '388, '389
                  Forex Computer Corp. FRX36C100
                  Silicon Integrated System (SiS) 85C310.


        1.4.4 Locked Configuration Registers       

        Some  memory  controllers  are  designed  so  that  they  can  be
        "locked"  at the end of the main bios initialization, requiring a
        hardware  reset  to  unlock,  and  thus  preventing The Last Byte
        Memory Manager from accessing the controller.  

        Examples: Intel 82335, 82335SX


        1.4.5 Configuration I/O Ports Reassigned      

        Some  memory  controllers  are  designed so that the "index/data"
        pair  of I/O ports used to access the configuration registers can
        be  reassigned  to  different  I/O  addresses.   This  makes  the
        configuration  registers  effectively  inaccessible  to  The Last
        Byte  Memory  Manager since it has no way of knowing what new I/O
        port addresses may have been established within the main bios.  

        Examples: Texas Instruments TACT84500
                  GS Technology GS62CS03
















        Copyright (C) 1990-94, Key Software Products. All Rights Reserved