WHAT'S NEW IN VERSION 2.41


Version  2.41  is  basically a maintenance release to correct some problems
discovered in version 2.40: 

     o  CHIPSET.EXE,  LASTBYTE.SYS:  Added  support  for  the  UNIchip
        U4800VLX,  which  is functionally different from the (non-VLX)
        U4800  predecessor.  CHIPSET used to identify both as a U4800,
        but  unfortunately the low-level physical driver for the U4800
        won't  work for the U4800VLX.  CHIPSET now distinguishes these
        two  chipsets,  and  a  new low-level physical driver just for
        the U4800VLX has been added to LASTBYTE.SYS.  

     o  HIGHUMM.SYS:  Wouldn't  allocate UMB's even though it reported
        that   UMB   memory   was  available.   A  necessary  but  not
        sufficient  condition  for  this to occur was that HIGHUMM had
        "split"  (placing  most of its code in R/O memory, Bank-Switch
        Memory,  or  the  HMA), and could be corrected in version 2.40
        by  use  of  the "/NOSPLIT" command line option.  This bug has
        been  corrected,  and  the  command  line  option is no longer
        needed.  

     o  CHIPSET.EXE:  The Headland/G2 HT113 was incorrectly identified
        as a HT103.  Corrected.  

     o  LASTBYTE.SYS:   Corrected   bugs  in  the  low-level  physical
        drivers  for  the HINT CS8001 and CS8005, and the OPTi 82C463,
        82C499,  82C801,  and  82C802.   The  bug  in  the 499/801/802
        driver  was mismatched PUSH and POP instructions, which caused
        the  driver  to  hang on initialization.  No problems had been
        observed  with  the  other  chipsets  listed, but I found that
        they  contained  code  that  should  have  been protected by a
        PUSHF/CLI...POPF sequence; this protection has been added.