TECHNICAL INFORMATION FOR PROGRAMMERS
                    -------------------------------------

      2M access always directly to NEC765 diskette controller chip and 8237
DMA controller. But you haven't to do the same!.  The standard DOS and BIOS
functions still works when 2M is installed, supporting new diskette formats
as standard ones.  If you need to format a 2M diskette from your high-level
applications, this is possible also via standard INT 13h function 5.

      When 2M is installed on memory,  INT 13h  service 5 becomes increased
its functionality. To find 2M resident on memory:

         Load AL with 0.
         Load ES:DI with 1492h:1992h.
         Load AH with a value from 0C0h to 0FFh.
         Call INT 2Fh.

      When INT 2Fh returns, if AL=0FFh and ES:DI points a "CiriSOFT:2M:2.0"
null terminated string...  2M is in memory!.   Note that ':' is a delimiter
and not always CiriSOFT will be  the  manufacturer  (I recomend search only
for the ":2M:" substring).  You can begin scanning with AH=0C0h and, if not
found 2M there, continue with AH=0C1h and so on. If 2M has been loaded from
booting a 2M disk, format functions are not available  (and 2M installation
check will correctly fail).

      When you had detected 2M on memory,  you can call to INT 13h function
5 to format a diskette track.  This  is easiest than standard BIOS service:
you don't need to select the disk density,  media,  or  last  sector in the
track. Of course, the standard BIOS function is still available but you can
call INT 13h as bellow:

         Load AH with 5.
         Load AL with 7Fh.
         Load CH with track number.
         Load DH with head number.
         Load DL with drive number.
         Load SI with 324Dh signature ("2M").
         Load ES:BX pointing to boot sector of future 2M diskette.

      Note that in standard BIOS call, AL sets the number of sectors (never
is 7Fh) and SI is not necesary equal to 324Dh.  This lets 2M to detect your
intention. You have not to fill big tables on ES:BX, simply point to a boot
sector  of  future diskette. This boot sector can be obtained from standard
2M diskette already formatted. New INT 13h format function return the sames
codes in AH that the BIOS standard routines.  Since 2.0 version of 2M,  the
track 0  head 0 contains a virtual BOOT sector in the first physical sector
of FAT2, and in high and extra-high density diskettes the SuperBOOT code in
the second-sixth sectors of FAT2.  The FAT2 is emulated using FAT1 instead.
The real BOOT sector is never shown in BIOS normal functions, and SuperBOOT
code also can not be accessed through BIOS standard functions.  The virtual
boot sector is equal to real one when 2MF formats a diskette,  but  can  be
altered by SYS command, for example. If you desire to format a 2M diskette,
and you want to make this diskette capable of SuperBOOT, you must write the
real BOOT sector, the virtual BOOT sector *AND* the SuperBOOT code. This is
possible using a little trick: when calling standard BIOS functions (read &
write), select the 128 or 129 head (instead 0 and 1 ones).  This lets 2M to
know  your  intention, and physical sectors will be read or written without
emulations.  Note that first track of 2M diskette has less sectors than the
rest,  so you must access no more than 1 (boot) + N (FAT1) + 1 (the virtual
BOOT) + 5 (SuperBOOT code) = 7 + N sectors ... and with double density only
must be accessed boot, FAT1 and virtual BOOT (no SuperBOOT code!).

      If disk is formatted using the STV technology (when offset 65 of boot
record is equal to 1)  the completely track must be written after format to
avoid future CRC errors on read.  This  does not is necessary on cylinder 0
side 0. In cylinder 0 side 1 the track must be write using head 81h instead
head 1. STV technology is used by 2MF if /M switch is present.

      You don't need to build your own boot  sectors,  buf if you decide to
modify something, you must know:

     - 2M diskettes have always  TWO FAT  copies,  for hardware reasons. Do
       not try to alter this specification (yes, for *hardware* reasons).
     - Modifing system ID probably makes 2M not able to detect the diskette,
       and standard BIOS will report sector-not-found errors.
     - Yoy can modify the jump instruction at the begin  of  boot,  and the
       boot code located after destination of this jump.  But  data located
       from offset 63 to last byte before boot code is covered by checksum,
       and you have to compute it if you modify something (the arithmetic 8
       bits add off all bytes must be zero, use checksum byte to force it).
     - Resuming: you can only modify offsets from 0 to 2, from 11 to 61 (it
       is not recommended) and the boot code.
     - If you try to write a boot sector with 2M installed, you will really
       write the virtual boot sector, instead the real one.  With 2M loaded
       on memory, the real boot sector can be modified only invocating BIOS
       write function in head 128 or 129 (instead 0-1).  The  virtual  boot
       sector is located on first sector of the second FAT copy (when 2M is
       loaded, all BIOS access to second copy of FAT are emulated using the
       first copy instead).  This  trick  makes  2M compatible with DOS SYS
       command. And  much  more, the first track of 2M diskette has the DOS
       standard format, with less space free where don't have room to place
       the completely FAT2.
     - If  the  boot  sector has a invalid checksum, a 'seek error' will be
       reported.
     - The virtual boot sector can be modify without problem, inside of the
       reason limits.  Note  that  with 2M installed you can access to this
       sector via standard DOS functions (sector 0) or BIOS (track 0 head 0
       and sector 1), never through FAT2 ... this is *emulated* by 2M (this
       emulation is only skipped while using head 128-129 instead 0-1).

      Here are the format of 2M diskettes, in order to meet your curiosity;
2M is not a secret or magic program!.  See  the  source code files for more
information (if you don't understand the source code comments, you may come
to Spain next summer :) ).

 * BOOT SECTOR OF 2M DISKETTE (COMMON TO ALL FORMATS).

          Assembler                        Comment                 Offset
      ---------------------  ----------------------------------  ----------
        JMP   BootP           ; 3 bytes                                0
        DB    "2M-STV08"      ; system ID of 2M 1.80M diskette         3
        DW    512             ; bytes per sector                      11
        DB    1               ; sectors per cluster                   13
        DW    1               ; sectors reserved at beginning         14
        DB    2               ; number of FAT copies                  16
        DW    224             ; root directory entries                17
        DW    3772            ; total sectors on disk                 19
        DB    0F0h            ; media descriptor                      21
        DW    11              ; sectors ocupied by each FAT           22
        DW    23              ; sectors per track                     24
        DW    2               ; number of heads                       26
        DD    0               ; special sectors reserved              28
        DD    0               ; number of sectors (32 bit drives)     32
        DB    0               ; physical drive                        36
        DB    0               ; reserved                              37
        DB    29h             ; DOS >= 4.0 diskette                   38
        DD    4B368A0Eh       ; serial number (random)                39
        DB    "NO NAME    "   ; disk label                            43
        DB    "FAT12   "      ; FAT type                              54
        DB    0               ; reserved by 2M                        62
        DB    0               ; 2M checksum (if used)                 63
        DB    7               ; format version (>=7 if virtual BOOT)  64
        DB    1               ; 1 if write track after format         65
        DB    0               ; data transfer rate on track 0         66
        DB    0               ; data transfer rate on track<>0        67
        DW    BootP           ; offset to boot program                68
        DW    Infp0           ; T1: information for track 0           70
        DW    InfpX           ; T2: information for track<>0          72
        DW    InfTm           ; T3: tracks sectors size table         74

 * NORMAL FORMATS (820/1476/984/1804K). FOR EXAMPLE: 1804K.

  Infp0 DB    19, 70          ; number of sectors / GAP 3 for format
        DB    1,2,3,4,5,6,7,8 ; sectors ordered (20..22 does not exist)
        DB    9,10,11,12,13,14
        DB    15,16,17,18,19
  InfpX DB    11, 40          ; number of sectors / GAP3 for format
        DB    3               ; sector size
        DB    1, 2            ; sector slidding (override by 2MF /X /Y)
  InfTm DB    3,3,3,3,3,3     ; size of sectors 1, 2, 3,...
        DB    3,3,3,3,3
  BootP:...                   ; SuperBOOT loader

 *  MAXIMUM CAPACITY FORMATS (902/1558/1066/1886K). FOR EXAMPLE: 1886K.

  Infp0 DB    19, 70          ; number of sectors, GAP3 for format
        DB    1,2,3,4,5,6,7,8 ; sectors ordered (20..23 does not exist)
        DB    9,10,11,12,13,14
        DB    15,16,17,18,19
  InfpX DB    64, 3           ; number of sectors / GAP3 for preformat
        DB    7               ; number of sectors to renum
        DB    128+1,  4, 4    ; renum table:
        DB    128+12, 1, 4    ; number of sector, new number, size
        DB    128+23, 5, 4
        DB    128+34, 2, 4
        DB    128+45, 6, 3
        DB    128+51, 3, 4
        DB    128+62, 7, 2
  InfTm DB    4,4,4,4,4,3,2   ; size of sectors 1, 2, 3,...
  BootP:...                   ; SuperBOOT loader

>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>

            2M format function in Ralf Brown Interrupt List format:

<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<

--------B-13057FSI324D-----------------------
INT 13 - 2M - FORMAT TRACK
        AX = 057Fh
        SI = 324Dh ("2M")
        CH = track number
        DH = head number
        DL = drive number
        ES:BX -> boot sector of future 2M diskette
Return: CF set on error
        CF clear if successful
        AH = status (see AH=01h)
Program: 2M is a TSR developed by Ciriaco Garcia de Celis to support
          non standard diskettes with 820-902/1476-1558K (5.25 DD/HD)
          and 984-1066/1804-1886K/3608-3772K (3.5 DD/HD/ED)
Notes:  it is not necessary to call AH=17h/AH=18h first (will be ignored)
        diskette format must begin always on cylinder 0 head 0
        the installation check for 2M must search a "CiriSOFT:2M:2.0" string or
          similar (recomended ":2M:" substring) in CiriSOFT TSR interface
        the boot sector can be obtained from a 2M diskette already formatted if
          reading (AH=02h) with head number 80h since 2M 2.0 (else use head 0)
        since 2.0 version of 2M, the BOOT sector is emuled using first physical
          sector of FAT2; the second-sixth physical sectors of FAT2 in HD or ED
          diskettes store the SuperBOOT code. To skip the FAT2 emulation (using
          FAT1) of 2M, in order to read the SuperBOOT code, head number must be
          80h-81h instead 0-1 (bit 7 active) in standard read/write functions.
          This lets diskcopy programs to format 2M target diskettes copying
          SuperBOOT code. If target diskette is already 2MF formatted (provided
          of boot code) this trick it is not necessary
        when using STV technology (offset 65 of boot sector equal to 1) it is
          necessary to write the full track before formatting (except track 0
          side 0) to complete the format and skip future CRC errors on read; in
          track 0 side 1 the head used must be 81h instead 1. Diskcopy programs
          may do a format-write-verify secuential phases to improve performance
SeeAlso: AH=05h"FLOPPY",INT 2F"CiriSOFT TSR interface"