Vfast             Technical Reference Manual           Page 1

                                  vFAST v1.5
            Copyright 1993-94 (c) International TeleCommunications
                              All Rights Reserved

                                 Introduction

         vFAST  was designed specifically for v32, v32bis,  and  vFAST
         modems. You should not attempt to use vFAST with a 2400  baud
         modem  unless your modem is error correcting.   The reason, a
         single  error could produce a resend request for as  much  as
         8192  bytes. It COULD be as little as 256 bytes but the  risk
         of 8192... well that is up to you.

         vFAST needs ONE of the following:

         16550 Uart
         Intelligent Digiboard (2, 4, 8, or 16 port).
         Intelligent Stargate.
         Intelligent Arnet.

         If you don't have one of the above, well try  and see.   You
         MIGHT be able to keep up but I doubt it.

         vFAST  is just what the name implies, a vERY  FAST  protocol,
         it'll run circles around Zmodem.

         vFAST  uses  DUAL 16 bit CRC's to protect  data.  Each  SHORT
         block  of  data  has a 16 bit CRC and every  8192  bytes  has
         another 16 bit crc. In short, CRC's inside of CRC's. Just  as
         effective  as  one single 32 bit crc but has  much  less  CPU
         overhead.

         vFAST  has RESTART recovery for aborted transfers as well  as
         SKIP for files you ALREADY have.

         You can ABORT a transfer by pressing ESC. Again, to keep  CPU
         overhead  low, we only check the  keyboard every  8  to  16K,
         depending on the status of the RX/TX buffers, so there may be
         a  short  delay   between  the time you  press  ESC  and  the
         program acknowledges the ESC.

         Once you see the acknowledgment, nothing may appear to happen
         for upwards of 10 to 12 seconds. vFAST is attempting to clear
         out the RX buffer and phone lines before exiting, to  prevent
         garbage  from spraying all over your screen.









         Vfast             Technical Reference Manual           Page 2

                             Hardware Requirements

         You need a 386, 486, or Pentium processor. vFast will NOT run
         on a 8088 or 80286 micro processor.

                             Command Line Switches

         vFAST supports the following command line switches:

         -Tx            Use Timeslicing when you cannot send or
                        receive anything. x is the TYPE of time
                        slicing. Valid TYPES are:

                        D         Desqview
                        O         OS-2
                        W         Windows

                        If  you use OS-2 or Windows Time Slicing,  you
                        must have have  DPMI turned on.

         -Bxxxxx        xxxx is the connect baud rate.

         -Pxxx          xxxx is the serial port, 1-4 if using the
                        standard internal driver.

         -Lxxxx         xxxx is Serial LOCK rate, 9600 - 115200.

         -S  <Fnames>   Start Sending files. Fnames is the  names  of
                        the  files  to  send.  Each  name  should   be
                        separated  by a single blank space. If  Fnames
                        is  prefixed  with an AT sign, @,  vFAST  will
                        ASSUME  Fnames is the name of a  SEND  control
                        file.

                        E.g.  -S @C:\TERM\SEND.CTL

                        SEND.CTL would be a text file listing the
                        files to send, one per line. Drive, path,
                        and DOS wildcards supported.

                        This must be the LAST command line switch used.

         -D<TYPE>       The TYPE of serial driver to use. Valid <TYPE>
                        are:

                        D       Digiboard
                        S       Stargate
                        A       Arnet

                       The default is the internal (Standard DOS  type
                       serial ports) highspeed serial driver.



         Vfast             Technical Reference Manual           Page 3

         -N*N          If you're running vFAST as a protocol driver
                       with Osiris XLT, include this switch.


         -R            Begin Receiving, must be the LAST command line
                       switch used.

         -K            Disable Keep Aborted Transfers. The default it
                       to keep all partial transfers. If you use this
                       driver as an external protocol driver for a BBS
                       you'll  want  to include this  on  the  command
                       line.

         -U<PATH>      This tells vFAST to place all files you receive
                       in   THIS  directory.  This  feature  is   ONLY
                       available if you register vFAST.

         -!<FILENAME>  This tells vFAST to pull the callers name from
                       DOOR.SYS, DOOR1.SYS, DOOR2.SYS, etc. This file
                       must be in DOOR.SYS format and you must supply
                       the full drive, path, AND filename.

                       E.g.  -!C:\PCBOARD\DOOR.SYS

                       NOTE:   This  feature  is  only  available   in
                       REGISTERED mode.

         -W<LOGFILE>   This allows you to redirect the log file to any
                       drive, directory, and file. You must supply the
                       full drive, path, AND filename.

                       E.g.  -WC:\PCBOARD\JOHN.LOG

                       NOTE:   This  feature  is  only  available   in
                       REGISTERED mode.

         -C<IRQ,ADDR>  Lets you reconfigure the IRQ and BASE  address
                       for the serial port. IRQ and ADDR are in  BASE
                       10 format.

                       E.g. -C3,744

                    Command Lines For Sending And Receiving

         The  minimum  command  line for RECEIVING  a  file  would  be
         something like this:

         vFAST -B<BaudRate> -L<LockRate> -P<Port Number> -R

         How  you  pass  the parameters will vary  depending  on  your
         terminal  software or bbs software. Check  the  documentation
         that came with your terminal or bbs software for specifics.


         Vfast             Technical Reference Manual           Page 4

         Assuming  your BBS/Terminal requires batch files  and  passes
         baudrate  in  %1,  port  number in  %2  then  you  might  use
         something like this:

         vfast -B%1 -L57600 -P%2 -R

         The  minimum  command  line  for  SENDING  a  file  would  be
         something like this:

         vFAST -B<BaudRate> -L<LockRate> -P<Port Number> -S <Ctl Filename>

         Notice, and this is VERY important, the space between -S  and
         <Ctl  Filename>. If you forget to put a space there,  nothing
         will happen.

         How  you  pass  the parameters will vary  depending  on  your
         terminal  software or bbs software. Check  the  documentation
         that came with your terminal or bbs software for specifics.

         Assuming your BBS/Terminal passes baudrate in %1, port number
         in  %2,  and the name of the file in %3, then you  might  use
         something like this:

         vfast -B%1 -L57600 -P%2 -S %3

             Examples of how to install vfast.exe with Osiris XLT

         Example of an Osiris XLT Rcv cmdline:

         VFAST -B*B -L*L -N*N -P*P -K -R

         Example of an Osiris XLT Send cmdline:

         VFAST -B*B -L*L -N*N -P*P -S @*U

                         Sample Batch Files For BBSes

         The  requirements  are clearly outlined above.  If  you  need
         help  installing vfast do not ask us. You should contact  the
         people  that designed your BBS software. We will only  answer
         questions directly related to vFAST itself.

                                   Shareware

         vFAST is shareware. Meaning you can use it for up to 30  days
         without  registering  it. When you finish your  download,  or
         uploads,  the  shareware version will pause for  10  seconds.
         Registering  vFAST  removes  this delay and  enables  the  -U
         switch.


                               vFAST Order Form

         Send $15.00 (US Currency) to:

                       International TeleCommunications
                                302 W. Mckinley
                          Poplar Bluff Mo. 63901-6372
                           United States Of America


         Register To (___________________________________)


         A  registration key will be placed on our BBS at  (314)  686-
         0120 in file area #15. The key will be password protected  so
         only YOU can download it. To reach this area, press F at  the
         MAIN  menu. When you reach the file area, press A then  enter
         15 and press RETURN.

         What Password do you want to use?   (________)