****************************** GRAPHICS *************************************

ASMLIB Graphics (C) Copyright 1991 - 1993 Douglas Herr
All rights reserved

ASMLIB recognizes and automatically supports several graphics modes,
including several which are not recognized by IBM's BIOS.  You should
assume that all ASMLIB graphics subroutines write directly to the video
hardware.  IMPORTANT: ALL ASMLIB GRAPHICS SUBROUTINES ASSUME DS:@DATA.

Locations on Graphics screens are defined by coordinate pairs such as (x,y).
X-coordinates are the horizontal dimensions of the screen, and Y-coordinates
are the vertical coordinates.  X = 0 is the at the left edge of the screen,
and X = 719 is the right edge of a Hercules screen, while Y = 0 is the top
edge of the screen and Y = 347 is the bottom (Hercules).  Thus, the
coordinate specified by (719,0) is the extreme upper right corner of a
Hercules screen.

BitBlock subroutines in ASMHUGE.LIB work with huge data blocks (larger
than 64k).  This permits entire EGA, VGA or InColor screens to be saved
in one block if sufficient RAM is available.




Graphics subroutines as powerful and flexible as ASMLIB's can be quite
large.  If you have licenced ASMLIB source code, you can use several
pre-defined conditional assembly directives to eliminate code from
ASMLIB object files if you do not want or need to support all graphics
modes:

        NOHERC      eliminates all Hercules and InColor code
        NOINCOLOR   eliminates code for the InColor card
               (InColor works with Hercules monochrome code in 2 colors)
        NO256       eliminates code for the three 256-color modes
        NOCGA       eliminates code for CGA graphics modes
        NOMCGA      elimiates code for MCGA mode 11h
        NOLPATTERN  elimiates code for non-solid lines (in DRAWLINE.ASM)

for example, if you want line drawing programs to use only EGA/VGA-type
16-color modes, assemble DRAWLINE.ASM like this:

         C:\MASM\>masm /dnoherc /dnocga /dno256 /dnomcga drawline;

this reduces the size of drawline.obj significantly and speeds its
operation somewhat.

If you want to support only 16-color EGA/VGA-type modes, you may also use
the EVGA*.LIB libraries to eliminate much of the code and data required
for monochrome, InColor, CGA and 256-color modes.  The EVGA*.LIB libraries
can eliminate several thousand bytes from your executable files.

Example:

LINK /NOE mycode.obj,,,EVGA86M+ASMLIB;

When using the EVGA* libraries, the EVGA* library must appear before
ASMLIB on the command line so that LINK uses the subroutines in the EVGA
library instead of the general subroutines in ASMLIB.  You must also use
LINK's /NOE switch.

The EVGA* libraries are provided with standard ASMLIB registration:

EVGA86T.LIB      for all PCs, tiny model
EVGA86S.LIB      for all PCs, small model
EVGA86M.LIB      for all PCs, medium model
EVGA86H.LIB      for all PCs, huge model
EVGA286T.LIB     for 286 or better PCs, tiny model
EVGA286S.LIB     for 286 or better PCs, small model
EVGA286M.LIB     for 286 or better PCs, medium model
EVGA286H.LIB     for 286 or better PCs, huge model



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

Graphics modes and pages supported are:

Mode           Maximum x   Maximum y   Colors  Pages (1)  Equipment
                ("xmax")    ("ymax")

HGraph           719          347       2         0, 1    HGC, HGC+ (2)
HGraph           719          347      16         0, 1    InColor  (2)
04h, 05h         319          199       4         0       CGA, EGA, MCGA, VGA
06h              639          199       2         0       CGA, EGA, MCGA, VGA
0Dh              319          199       16        0 - 7   EGA, VGA  (3)
0Eh              639          199       16        0 - 3   EGA, VGA  (3)
0Fh              639          349       4         0       EGA, VGA  (4)
10h              639          349       16        0, 1    EGA, VGA  (3,5)
11h              639          479       2         0       MCGA, VGA
12h              639          479       16        0       VGA
13h              319          199       256       0       MCGA, VGA
40h              639          399       2         0       ATT 6300
6Ah              799          599       16        0       VESA  (6)
XMode16      up to 799     up to 599    16        0       Super EGA/VGA
VGA13X      319 or 359    199 to 479    256       (7)     VGA
SVGA16      799 or 1023   599 or 767    16        0       Super VGA (8)
SVGA256     639 to 1023   399 to 767    256       0       Super VGA (8)

(1) page numbering begins with page 0.  Several modes have sufficient
    memory available for additional page(s).
(2) page 1 available after calling Use64k
(3) EGA pages assumes 256k EGA memory
(4) monochrome monitor only
(5) EGA with 128k or more memory
(6) VESA6A is supported by many Super VGA cards with multi-frequency
    monitors
(7) VGA13X pages available range from 0 to 3.  See VGA13X in MODE.DOC.
(8) requires VGAKIT-compatible Super VGA and multi-frequency monitor.  See
    WhichVGA in SYSTEM.DOC and SVGA16 and SVGA256 in MODE.DOC.


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BEZIER:        draw a Bezier curve on the screen
Source:        bezier.asm (drawline.asm)

80x87 or emulator required

Call with:     DS:[BX] pointing to curve coordinate data
               CX = number of points on curve (0 < CX < 32768)
                a larger number of points on the curve will result in
                slower operation and a smoother curve.  In many cases
                CX > 50 will not improve the appearance of the curve.

                Four coordinates are required: two curve endpoints and
                two control points.  The curve endpoints (x0, y0) and
                (x3, y3) are similar to DrawLine's coordinates; if you
                call bezier with CX = 1, you will see only a straight
                line between the endpoints.  The "control points" act
                like magnets, pulling the curve away from a straight line.
                At each endpoint, the curve is tangent to a line drawn
                between the endpoint and the adjacent control point
                ("adjacent" control point meaning adjacent in the data
                structure).

Returns:       nothing
Uses:          all 80x87 registers
Supports:      all ASMLIB graphics modes; drawmode 0 not recommended
Example:

extrn  bezier:proc

.data
extrn  drawmode:byte
bz     dw 50,50            ; first endpoint:       (x0, y0)
       dw 100,0            ; first control point:  (x1, y1)
       dw 200,0            ; second control point: (x2, y2)
       dw 250,175          ; second endpoint:      (x3, y3)
                           ; note that both control points in this
                           ; example pull the curve toward the top of the
                           ; screen

.code
; program fragment assumes DS:@data, 80x87 is installed
; and that the screen is in graphics mode
       .
       .
       mov     drawmode,1  ; use foreground color
       lea     bx,bz       ; point to bezier curve data
       mov     cx,100      ; should be adequate
       call    bezier




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BITBLOCKBYTES: calculate bytes required to save a bit block
Source:        bbbytes.asm ($graph.asm)

Call with:     DS:[BX] pointing to x- and y-coordinate data (see example)
Returns:       DX:AX = bytes required to save the bit block
               small or medium model:
                  if CF = 0, bytes required is less than 64k segment
                     => no problem
                  if CF = 1, bit block is too big for a 64k segment
                     small or medium model BitBlock subroutines will
                     not work properly
Uses:          AX, DX, flags
Supports:      all ASMLIB graphics modes; call BitBlockBytes while
               the system is in the mode you intend to use.  Otherwise,
               an incorrect byte size may be returned, leading to either
               wasted memory or memory allocation errors.
Example:

include asm.inc

extrn   bitblockbytes:proc

.data
x0      dw 100,43         ; first corner at (100,43)
x1      dw 175,143        ; second corner at (175,143)

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea    bx,x0          ; DS:[BX] points to bit block corner data
        call   bitblockbytes  ; returns AX = byte size of buffer required
        jc     too_big        ; bit block is too big if CF = 1 (small or med)

; note that when the huge model is used, memory greater than 64k must be
; allocated with DOS function 48h.  See STARTUP.ASM to release unused
; memory to allow DOS memory allocation.



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BITPLANEBYTES: calculate bytes to save one plane of a bit block
               alternate entry to BitBlockBytes; calculates bytes
               required to save one plane of multi-plane modes
Source:        bbbytes.asm ($graph.asm)
Call with:     DS:[BX] pointing to x- and y-coordinate data
Returns:       DX:AX = bytes required to save the bit plane
               small or medium model:
                  if CF = 0, bytes required is less than 64k
                     => no problem
                  if CF = 1, bit plane is too big for a 64k segment
                     small or medium model BitPlane subroutines will
                     not work properly
Uses:          AX, DX, flags
Supports:      all ASMLIB graphics modes; call BitPlaneBytes while
               the system is in the mode you intend to use.  If the
               system is is not in a multi-plane mode, BitPlaneBytes
               will give you the same results as BitBlockBytes.
               Graphics modes with multiple planes are mode 0Fh (2 planes)
               and all 16-color modes (4 planes).
Example:

include asm.inc

extrn   bitplanebytes:proc

.data
x0      dw 100,43         ; first corner at (100,43)
x1      dw 175,143        ; second corner at (175,143)

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea    bx,x0          ; DS:[BX] points to bit block corner data
        call   bitplanebytes  ; returns AX = byte size of buffer required
        jc     too_big        ; unlikely



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BUFFERDIM:     change logical buffer dimensions
               does not change number of pixels displayed on screen;
               used with ScreenOrigin.
Source:        buffdim.asm ($graph.asm)

Call with:     DS:[BX] pointing to new buffer dimensions
               Note that the logical buffer dimensions should be
               greater than the dimensions displayed on the screen
               The logical buffer dimensions must not create a plane size
               greater than 64k; a logical pixel width of 800 + logical height
               of 600 works out to 60,000 bytes per plane.

               If anything is displayed on the screen before changing
               logical dimensions, it will be unreadable after calling
               BufferDim if your logical x-dimension is not the same as
               the screen's physical x-width.

               BufferDim does no error checking; you must determine if
               the computer has an EGA or VGA (see GetCRT in SYSTEM.DOC)
               and you must verify that the logical dimensions are greater
               than the screen dimensions.

               Using BufferDim disables ASMLIB's multiple graphics pages
               capabilities.

Returns:       nothing
Uses:          nothing; all registers and flags are saved
Supports:      EGA/VGA-type 16-color graphics modes
Example:       see next page




(BufferDim example)

; The computer has a 256k EGA card & EGA-only monitor 
; and I want to display an image that is 800 pixels wide
; and 600 pixels high.
; I'll use EGA mode 10h, switch to logical dimensions of 800x600,
; put the image in the video buffer & use ScreenOrigin to view
; various parts of the image

include asm.inc

public  mysub
extrn   bufferdim:proc, screenorigin:proc
extrn   loadpcx:proc

.data
dim     dw 800,600              ; I want 800 logical x
                                ;  & 600 logical y
xy      dw 0,0                  ; screen origin always starts at (0,0)
fname   db '800x600.pcx',0      ; a .PCX file with an 800 x 600 image

.code
mysub   proc
; set up 640x350 16-color mode
        mov    ax,10h           ; use BIOS to set mode
        int    10h
        lea    bx,dim           ; point to logical buffer dimensions
        call   bufferdim        ; set up 800x600 logical dimensions
                                ; NOTE: only one page available

; program loads image to video buffer
        lea    dx,fname         ; point to filename
        call   loadpcx          ; get image

; default screen origin: (0,0) of buffer is at (0,0) of screen
; change portion of buffer displayed to logical (100,100)
; at (0,0) of screen
        lea    bx,xy
        mov    word ptr [bx],100
        mov    word ptr 2[bx],100
        call   screenorigin



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CIRCLEASPECT:  modifies aspect ratio of circle
Source:        drawcirc.asm ($graph.asm)

Call with:     AH = numerator of aspect ratio
               AL = denominator of aspect ratio
               AH <> 0, AL <> 0

               CircleAspect is used with DrawCircle to draw an ellipse.
               An aspect ratio less than one makes a flat ellipse and an
               aspect ratio greater than one makes a tall ellipse.
               Aspect ratios greater than 5 or less than 1/5 may cause
               unpredictable results.

Returns:       nothing
Uses:          nothing; all registers and flags are saved
Supports:      all ASMLIB graphics modes
Example:       see DrawCircle



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DEFGMODE:      restore ASMLIB's internal flags to use system graphics
               mode (see ForceGMode)
Source:        defgmode.asm

Call with:     no parameters
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:       see ForceGMode




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DRAWCIRCLE:    draw a circle
Source:        drawcirc.asm ($graph.asm, $putdot.asm, divi2.asm, mulf4.asm,
               invi2.asm, i2tof4.asm, f4toi2.asm)

Call with:     DS:[BX] pointing to circle center coordinates and x-radius
               Drawmodes supported are:
                4 = AND the foreground color with the screen
                3 = OR the foreground color with the screen
                1, 2 = use foreground color
                0 = XOR circle with existing screen
               -1, -2 = use background color
               -3 = OR the background color with the screen
               -4 = AND the background color with the screen
               See DrawMode for more information.
               If you change the screen's logical dimensions with
               BufferDim, DrawCircle may not draw round circles;
               use CircleAspect to adjust the shape.

Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc
extrn   drawcircle:proc, circleaspect:proc

.data
xcenter dw 100              ; DrawCircle data must be words
ycenter dw 100              ; the circle is centered at (100,100)
xradius dw 50               ; x-dimension radius in pixels (>0)

.code
; program fragment assumes DS:@data
        .
        .
        .
        mov   ah,5
        mov   al,1          ; a tall ellipse
        call  circleaspect

        lea   bx,xcenter    ; DS:[BX] points to circle data
        call  drawcircle    ; draw the circle



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DRAWBOX:       draw a rectangle on a graphics screen
Source:        drawbox.asm ($graph.asm, $vert.asm, $horiz.asm, several others)

Call with:     DS:[BX] pointing to box corner data
               Drawmodes supported are:
                4 = AND the foreground color with the screen; color modes
                3 = OR the foreground color with the screen
                1, 2 = use foreground color: all modes
                0 = XOR foreground color with existing pixels
               -1, -2 = use background color: all modes
               -3 = OR the background color with the screen
               -4 = AND the background color with the screen; color modes
               See DrawMode for more information; see also LinePattern
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   drawbox:proc

.data
x0      dw 25,10            ; first corner at (25,10); data is word size
x1      dw 301,97           ; opposite corner at (301,97)

.code
; program fragment assumes DS:@data
        .
        .
        lea   bx,x0         ; DS:[BX] points to box corner data
        call  drawbox



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DRAWLINE:      draw a line on a graphics screen
Source:        drawline.asm ($graph.asm, $vert.asm, $horiz.asm,
                             $loslope.asm, $hislope.asm, many others)

Call with:     DS:[BX] pointing to line endpoint data
               Drawmodes supported are:
                4 = AND the foreground color with the screen; color modes
                3 = OR the foreground color with the screen
                1, 2 = use foreground color: all modes
                0 = XOR foreground color with existing pixels
               -1, -2 = use background color: all modes
               -3 = OR the background color with the screen
               -4 = AND the background color with the screen; color modes
               See DrawMode for more information; see also LinePattern
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   drawline:proc

.data
x0      dw 25,10            ; first endpoint at (25,10); data is word size
x1      dw 301,97           ; other end of line at (301,97)

.code
; program fragment assumes DS:@data
        .
        .
        lea   bx,x0         ; DS:[BX] points to line coordinate data
        call  drawline



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DRAWMODE:      control ASMLIB graphics drawing mode
Source:        $graph.asm

               DrawMode is a public byte in DGROUP used to control the
               operation of many ASMLIB subroutines.  ASMLIB's default
               drawmode is 1.

               Typically, drawmodes have the following effects:
                2 = use foreground color only; text is printed without
                    background, foreground only of line patterns or
                    fill patterns is used
                1 = use foreground and background; text is printed with
                    background, line patterns and fill patterns update
                    both foreground and background
                0 = foreground color is XORed with the existing screen
                    (not supported in 256-color or CGA 4-color modes)
               -1 = characters or fill pattern drawn with foreground
                    and background reversed
               -2 = character or line drawn with background color only

Supports:      all ASMLIB graphics modes
Example:

include asm.inc

.data
extrn   drawmode:byte

.code
; program fragment assumes DS:@data
        .
        .
        mov     drawmode,2      ; print text with foreground color only



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FILLAREA:      fills an irregular area on a graphics screen
Source:        fillarea.asm ($graph.asm, $horiz.asm, $getdot.asm,
                             several others)

Call with:     DS:[BX] pointing to seed pixel coordinates

               Fills many irregularly-shaped areas with color and/or
               pattern, beginning at (x,y).  FillArea may not work
               properly with regions which have concave boundaries
               crossing horizontal lines.  The area's boundary is
               defined by a solid line of non-zero pixels.
               DrawModes supported are:
                2 = fill with foreground color only (if fill pattern
                    has been defined): 16-color modes
                1 = fill with foreground (and background, if fillpattern
                    defined): all modes
               See also FillPattern.
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   fillarea:proc

.data
x       dw 10,15         ; start fill operation at x=10, y=15

.code
; program fragment assumes DS:@data
        .
        .
        lea    bx,x
        call   fillpattern



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FILLBOX:       draw a filled rectangle on a graphics screen
Source:        fillbox.asm ($graph.asm, $horiz.asm, several others)

Call with:     DS:[BX] pointing to box corner data
               Drawmodes supported are:
                4 = AND the box with the pre-existing screen
                3 = OR the foreground color with the screen
                1, 2 = use foreground color
                0 = XOR foreground color with existing pixels
               -1, -2 = use background color
               -3 = OR the background color with the screen
               -4 = AND the background color with pre-existing screen
               See DrawMode for more information; also see FillPattern.
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   fillbox:proc

.data
x0      dw 25,10            ; first corner at (25,10); data is word size
x1      dw 301,97           ; opposite corner at (301,97)

.code
; program fragment assumes DS:@data
        .
        .
        lea   bx,x0         ; DS:[BX] points to box corner data
        call  fillbox



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FILLPATTERN:   define an optional pattern for FillArea & FillBox
Source:        fpattern.asm

Call with:     DS:[BX] pointing to ASCIIZ pattern string.
               Up to 8 characters in the string will be used.
               The pattern must be re-defined before each call to a line
               drawing subroutine (FillArea, FillBox).
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes except 256-color modes
Example:

include asm.inc

extrn   fillbox:proc
extrn   fillpattern:proc

.data
x0      dw 25,10            ; first corner at (25,10); data is word size
x1      dw 301,97           ; opposite corner at (301,97)
pattern db 8 dup(10101010b),0

.code
; program fragment assumes DS:@data
        .
        .
        lea   bx,pattern    ; DS:[BX] points to pattern string
        call  fillpattern   ; define the pattern
        sub   bx,8          ; DS:[BX] points to box corner data
        call  fillbox       ; draw a patterned box



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FORCEGMODE:    force ASMLIB to use one particular graphics mode
               this is handy for two-monitor systems
Source:        defgmode.asm

Call with:     AL = graphics mode to use
               forcegmode does not change the actual screen mode; what
               it does is to force ASMLIB's central graphics control
               to ignore the system mode.  Call defgmode to restore
               ASMLIB's internal flags to the default state.
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes (256-color modes not tested)
Example:

include asm.inc

extrn   modecolor:proc, modemono:proc
extrn   forcegmode:proc, gcolor:proc, defgmode:proc

.data
gtext   db 'Graphics mode',0
gpos    dd 0                   ; 2 words of zeros to position text
ttext   db 'Text mode',0

.code
; program fragment assumes DS:@data
; I want text on the monochrome screen and 16-color graphics on the EGA
        call   modecolor       ; switch to color monitor
        mov    ax,10h          ; set up graphics mode
        int    10h
        mov    al,10h          ; tell ASMLIB to use mode 10h
                               ; use AL = 13h for VGA 256-color modes
                               ; use AL = 8 for Hercules (including InColor)
        call   forcegmode      ; best to do this after the mode change
        call   modemono        ; switch back to the monochrome monitor
        mov    ax,010Ch        ; blue background, red foreground
        call   gcolor
        lea    si,gtext        ; point to graphics message
        lea    dx,gpos         ; positioned at upper left corner
        call   gprint          ; prints on EGA in graphics mode

        lea    si,ttext        ; point to text message
        xor    dx,dx           ; upper left corner of text screen
        mov    ah,7            ; normal color
        call   tprint          ; display message on monochrome monitor
        .
        .
; sometime later, all done with this setup
        call   defgmode        ; clear ASMLIB's internal graphics flags



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GBASESEG:      change ASMLIB graphics base segment
Source:        gbaseseg.asm ($graph.asm)

Call with:     AX = base segment address for alternate buffer
               if AX = 0, default base segment is restored
               GBaseSeg may be used to create and update off-screen graph
               images, thus simulating multiple screen pages.
Returns:       nothing
Uses:          nothing
Supports:      mode 04h, 05h, HGraph (monochrome only), 40h, 11h, 13h

               buffer size requirements:

                mode 04h, 05h    16384 bytes
                HGraph, 40h      32768 bytes
                mode 11h         38400 bytes
                mode 13h         64000 bytes

                GBaseSeg may also work with planar or bank-switched
                modes in a windowing multi-tasking environment, such
                as DesqView.  Feedback, please!!
                You must call GBaseseg AFTER switching the system to graphics
                mode, or it will not work; you must also call GBaseSeg with
                AX = 0 before changing from one graphics mode to another, or
                the default base segment may get messed up.
Example:

.model medium

public myprog
extrn  gbaseseg:proc, drawbox:proc

.data
boxdata dw 0,0,319,199

.fardata
screen1 db 64000 dup (0)     ; second screen for mode 13h

.code
myprog proc
; program fragment assumes DS:@DATA
; mode 13h, 320x200x256 colors
       mov     ax,13h
       int     10h
; use alternate buffer
       mov     ax,seg screen1
       call    gbaseseg
       lea     bx,linedata
       call    drawbox


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GCENTER:       centers a string on a graphics screen
Source:        gcenter.asm (gprint.asm, $graph.asm, strlen.asm, f8x14.asm)

GCENTERX:      centers a double-width string on a graphics screen
Source:        gcenterx.asm (gprintx.asm, $graph.asm, strlen.asm, f8x14.asm)

Call with:     DS:[SI] pointing to the string to print
               DS:[DX] pointing to x- and y-coordinates
               the x-coordinate is a placeholder; GCenter calculates the
               correct x value before calling GPrint.

               Colors, drawmodes and character sizes are the same as
               for GPrint or GPrintX.
Returns:       x = calculated x-coordinate
Uses:          nothing; all registers and flags are saved.
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   gcenter:proc

.data
x       dw ?
y       dw 2               ; print graph title 2 pixels down from the top
title   db 'Graph title',0

.code
; program fragment assumes DS:@data
        .
        .
        lea    si,title    ; DS:[SI] points to string
        lea    dx,x        ; point to coordinates
        call   gcenter     ; print the string, centered horizontally



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GCLEAR:        clears the active portion of a graphics screen
               uses background color
Source:        gclear.asm ($graph.asm, $horiz.asm, others)

Call with:     no parameters
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   gclear:proc

.code
        .
        .
        .
        call  gclear

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GCOLOR:        update color used by ASMLIB graphics
Source:        gcolor.asm ($graph.asm)

Call with:     AL = foreground color
               AH = background color

               for 4-color modes, colors may be 0-3
               for 16-color modes, colors may be 0-15
               for 256-color modes, colors may be 0-255

Returns:       nothing
Uses:          nothing
Supports:      all color graphics modes and mode 0Fh
               GColor is ignored by 2-color modes
Example:

include asm.inc

extrn   gcolor:proc

.code
        .
        .
        .
        mov   ah,bcolor      ; background color
        mov   al,fcolor      ; foreground color
        call  gcolor



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GCOPY:         copies one page of graphics memory to another
Source:        gcopy.asm ($graph.asm)

Call with:     BH = frompage
               BL = topage
Returns:       CF = error flag
                if CF = 0, no error
                if CF = 1, bad page number or frompage = topage
Uses:          AX, CF
Supports:      Hercules and InColor (with Use64k)
               EGA/VGA modes 0Dh, 0Eh, 0Fh, 10h
               VGA13X [0,1,2]
Example:

include asm.inc

extrn   gcopy:proc

.code
        .
        .
        .
        mov   bx,0001h       ; copy from page 0 to page 1
        call  gcopy
        jc    bad_page       ; uh oh, pages not supported



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GCURSOR:       simulate text-mode cursor on graphics screen
GUCURSOR:      simulate underscore cursor on graphics screen
Source:        gcursor.asm ($graph.asm)

Call with:     DS:[DX] pointing to x- and y-coordinate word data
               x and y are the coordinates of the UPPER LEFT corner of
               a character block.  Note that text characters are
               8 x-pixels wide and from 8 to 16 y-pixels high.

               GCursor and GUCursor maintain the simulated cursor while
               the keyboard type-ahead buffer is empty.  GCursor shape
               is an underscore when INSERT is off and a larger block
               when INSERT is on.  GUCursor is an underscore regardless
               of the state of the INSERT toggle.
Returns:       nothing
Uses:          AX, CX
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   gcursor:proc, getkey:proc

.data
x       dw 10,20        ; put the cursor in the character block at (10,20)

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea   dx,x
        call  gcursor
        call  getkey    ; retrieve the key that was pressed



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETBITBLOCK:   saves a portion of a graphics screen in memory
Source:        bitblock.asm ($graph.asm, bb02.asm, bb04.asm, bb06.asm,
                             bb08.asm, bb10.asm, bb12.asm, bb14.asm,
                             lowES2hi.asm, lowDS2hi.asm)

Call with:     ES:[DI] pointing to memory buffer for the bit block
               DS:[BX] pointing to x & y coordinate data

               Note that a bit block copied from a 4-plane mode may
               only be restored to a 4-plane mode; likewise, a bit
               block saved from a 2-color mode should be restored to
               a 2-color mode or to a single bit plane of a 16-color
               mode.
Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
               memory models: small medium, huge


    If you do not intend to support all ASMLIB graphics modes, you can
    call mode-specific BitBlock subroutines to reduce .EXE size.
    These subroutines use the same calling parameters as GetBitBlock
    and PutBitBlock:


    getbb02: mode 04h, 05h, 11h, 40h, HGraph (mono and InColor)
    getbb06: mode 0Dh, 0Eh, 0Fh, 10h, 12h, SVGA16(0), XMODE16
    getbb08: mode 13h
    getbb10: VGA13X
    getbb12: SVGA16
    getbb14: SVGA256


    putbb02: mode 04h, 05h, 11h, 40h, HGraph (mono only)
    putbb04: HGraph (InColor only)
    putbb06: mode 0Dh, 0Eh, 0Fh, 10h, 12h, SVGA16(0), XMODE16
    putbb08: mode 13h
    putbb10: VGA13X
    putbb12: SVGA16
    putbb14: SVGA256

Example on next page



; example of GetBitBlock use

include asm.inc

extrn   bitblockbytes:proc, getbitblock:proc, putbitblock:proc
extrn   halloc:proc

.data
ptr     dw ?                ; use this to save pointer to bit block
x0      dw 100,43,175,143   ; save from (100,43) to (175,143)

.code
; program fragment assumes DS:@data
        .
        .
        lea   bx,x0         ; point to block corners
        call  bitblockbytes ; calculate byte requirement
        jc    too_big       ; error control
        call  halloc        ; this example allocate the buffer from heap
                            ; can't do this w/ huge bit blocks
        jc    no_memory     ; more error control
        mov   ptr,bx        ; save near address of bit block
        push  ds
        pop   es            ; ES = DS
        mov   di,bx         ; ES:[DI] points to buffer
        lea   bx,x0         ; DS:[BX] points to coordinate data
        call  getbitblock
        .
        .

; later . . .
        lea   bx,x0         ; put the bit block back where you found it
        push  ds
        pop   es            ; ES = DS
        mov   di,ptr        ; ES:[DI] points to buffer
        call  putbitblock


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETBITPLANE:   saves one plane of a bit block in memory
Source:        small & medium: bitplane.asm ($graph.asm, bb02.asm, bb04.asm
                               bb06.asm, bb08.asm, bb10.asm, bb12.asm,
                               bb14.asm)
               huge: same as small & medium, + lowES2hi.asm & lowDS2hi.asm

Call with:     ES:[DI] pointing to memory buffer for the bit block
               DS:[BX] pointing to x & y coordinate data
               AL = plane number to save
               valid plane numbers are 0 - 3 in 16-color modes
                                       0 & 2 in EGA monochrome mode

               In 16-color modes, EGA/VGA and InColor planes are:
                0 = blue, 1 = green, 2 = red, 3 = gray (or intensity)
               In EGA monochrome mode, plane 0 = normal, plane 2 = blink
                or intensity
               The actual colors each plane represents may change
               depending on the values in the pallete registers.

Supports:      all 16-color modes plus EGA monochrome
               other modes: GetBitPlane works like GetBitBlock
               memory models: small, medium, huge



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETVIEW:       returns a pointer to the current view coordinates for
               the active page
Source:        getview.asm ($graph.asm)

Call with:     no parameters
               most ASMLIB subroutines, except the GPrint series, Gload,
               GCopy and GSave, limit their activity to the view region.
               You may use the returned pointer to change the active
               portion of the screen; be careful not to exceed the maximum
               x1 and y1 values permitted by the current mode.  Also, x0
               must always be less than x1 and y0 must always be less than
               y1.
               ASMLIB's defaults are:
                x0 = 0
                y0 = 0
                x1 = xmax
                y1 = ymax

               See also ResetView

Returns:       ES:[BX] pointing to the current view coordinates
Uses:          ES, BX; all other registers and flags are saved
Supports:      all ASMLIB graphics modes and pages
Example:

include asm.inc

extrn   getview:proc

x0 EQU word ptr ES:[BX]
y0 EQU word ptr ES:2[BX]
x1 EQU word ptr ES:4[BX]
y1 EQU word ptr ES:6[BX]

.code
        .
        .
        .
        call   getview



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETDOT:        determine pixel value on graphics screen
Source:        getdot.asm ($graph.asm, $getdot.asm, others)

Call with:     DS:[BX] pointing to pixel coordinate data
Returns:       if CF = 0, AX = pixel value
               if CF = 1, pixel coordinates outside active view area
Uses:          AX, CF
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   getdot:proc

.data
x       dw 10,10             ; pixel at (10,10)

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea    bx,x          ; point to pixel coordinates
        call   getdot        ; get pixel value
        jc     out_of_bounds ; oops




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GLOAD:         loads a graphics screen saved as a disk file by GSave
Source:        gsave.asm ($graph.asm, $gbytes.asm, $reset.asm)

Call with:     DS:[DX] pointing to the name of the file to load
               the filename must be an ASCIIZ string
Returns:       AX = MS-DOS error code
Uses:          AX, BX, CX, flags
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   gload:proc

.data
filename db 'graph.bin',0

.code
; program fragment assumes DS:@data
        .
        .
        lea   dx,filename
        call  gload



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GLOADEMS:      loads a graphics screen saved in EMS memory by GSaveEMS
Source:        gloadems.asm ($graph.asm, ems.asm, $gbytes.asm, $emspage.asm
                             banks.asm, $reset.asm, emputget.asm, $plane.asm,
                             $gloadx.asm, $plane.asm)

Call with:     BX = EMS handle
               assumes DS:@data
Returns:       if CF = 0, no error
               if CF = 1, AH = EMS error code
Uses:          AX, flags
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

public  testems

extrn   mode43:proc, getkey:proc, isems:proc, gsaveems:proc, gloadems:proc

.data
handle  dw 0

.code
testems proc
        mov     ax,12h          ; VGA 16-color mode
        int     10h
        .
        .
        .
; program draws screen
        .
        .
        call    isems
        jc      no_ems
        call    gsaveems
        jc      no_ems
        mov     handle,bx
        .
        .
; some time later ...
        mov     bx,handle
        call    gloadems
        jc      kill_ems
        call    getkey
kill_ems:
        mov     dx,handle
        mov     ah,45h          ; EMS function: de-allocate block
        int     67h

no_ems: call    mode43
        ret
testems endp
        end



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GLOADXMS:      loads a graphics screen saved in XMS memory by GSaveXMS
Source:        gloadxms.asm ($graph.asm, xms.asm, $gbytes.asm, $gloadx.asm,
                             banks.asm, $reset.asm, xmputget.asm, $plane.asm)

Call with:     BX = XMS handle
               assumes DS:@data
Returns:       if CF = 0, no error
               if CF = 1, AH = XMS error code
Uses:          AX, flags
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

public  testxms

extrn   mode43:proc, getkey:proc, isxms:proc, gsavexms:proc, gloadxms:proc
extrn   freexms:proc

.data
handle  dw 0

.code
testxms proc
        mov     ax,12h          ; VGA 16-color mode
        int     10h
        .
        .
        .
; program draws screen
        .
        .
        call    isxms
        jc      no_xms
        call    gsavexms
        jc      no_xms
        mov     handle,bx
        .
        .
; some time later ...
        mov     bx,handle
        call    gloadxms
        jc      kill_xms
        call    getkey
kill_xms:
        mov     bx,handle
        call    freexms

no_xms: call    mode43
        ret
testxms endp
        end



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GPAGE:         changes active and displayed graphics page
               GPage changes ASMLIB's default graphics page and displays
               the page.  See also UseGPage and ShowGPage.
Source:        gpage1.asm ($graph.asm, $herc.asm, gpage.asm)

Call with:     BL = page number.  See table at start of this GRAPHICS.DOC
               file.
Returns:       if CF = 0, no problem
               if CF = 1, bad page number requested
Uses:          CF
Supports:      EGA, VGA, Hercules, InColor: modes with more than one page
Example:

include asm.inc

extrn   gpage:proc

.code
        .
        .
        mov    bl,1          ; use and show page 1
        call   gpage
        jc     oops          ; uh oh, wrong mode


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GPRINT:        prints ASCIIZ string on a graphics screen
Source:        gprint.asm ($graph.asm, f8x14.asm, $gp00.asm, $gp02.asm,
                           $gp06.asm, $gp08.asm, $gp10.asm, others)

Call with:     DS:[SI] pointing to the ASCIIZ string
               DS:[DX] pointing to x- and y-coordinate data
               drawmodes supported by GPrint are:
                2 = foreground only; background pixels left alone
                1 = foreground and background pixels updated with
                    current gcolor
                0 = foreground color is XORed with the existing screen
               -1 = like drawmode 1, but foreground and background reversed
               -2 = like drawmode 2, but uses background color
               Any pixel position may be specified; does not wrap around
               from right side of screen to left.  Default character size
               is 8x8 for CGA modes and modes 0Dh, 0Eh and 13h, 8x14 for
               others.
               High ASCII characters are undefined in 8x8 pixel modes
               unless you call SmallText sometime earlier in the program.
Returns:       nothing
Uses:          CX; all other registers and flags are saved
Supports:      all ASMLIB graphics modes
               not all drawmodes supported with CGA modes 04h and 05h
Example:

include asm.inc

extrn   gprint:proc

.data
string  db 'print this, if you will',0
gpos    dw 0,0                          ; print at upper left corner

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea   si,string
        lea   dx,gpos
        call  gprint

additional GPRINT information on next page


GPRINT will work with user-defined fonts up to 16 pixel rows high in all
modes with ymax > 200.  GPRINT reads a public data area in DGROUP to
determine the SEGMENT:OFFSET address of the font data, the number of pixel
rows per character and the byte increment between sucessive character
definitions.  Characters must be 8 pixels wide.

FONTDATA.ASM has the required font data:

public  f14seg
f14seg  dw SEG f8x14    ; segment address of user-loaded font (8x14 default)
        dw OFFSET f8x14 ; offset address of user-loaded font (8x14 default)
        db 14           ; byte size of character
        db 14           ; bytes from start of one char to start of next

Example:

include asm.inc

.data
extrn   f14seg:word

fname   db 'c:\ramfont\italics.fnt',0   ; 8x14 characters
fbuffer db 4096 dup (0)                 ; all RAMFont fonts are 4096 bytes
; the fonts supplied by Hercules with the Graphics Card Plus and InColor
; card are a variety of sizes, but in each font file the byte increment
; is always 16 bytes

.code
        .
        .
        mov     ax,@data
        mov     ds,ax
        lea     dx,fname
        mov     ax,3D00h        ; open file for read
        int     21h
        mov     bx,ax           ; copy file handle to BX
        lea     dx,fbuffer      ; DS:[DX] points to buffer
        mov     cx,4096
        mov     ah,3Fh          ; read file
        int     21h
        mov     ah,3Eh          ; close file
        int     21h
        mov     f14seg,ds      ; update segment address of new font
        mov     f14seg+2,dx    ; update offset address of new font
        mov     f14seg+4,(16 shl 8) OR 14
                                ; 14-pixel row character
                                ; 16 bytes between character definitions


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GPRINTDOWN:    prints ASCIIZ string vertically on graph screen
GPRINTUP:      prints ASCIIZ string vertically on graph screen
Source:        gprint.asm ($graph.asm, f8x14.asm, $gp00.asm, $gp02.asm,
                           $gp06.asm, $gp08.asm, $gp10.asm, others)

Call with:     same as GPrint
               rotates each character 90 degrees and prints from top
               downward or from bottom upward.  Character size 8x8.

               Returned data and registers used same as GPrint
Example:       see GPrint.


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GPRINTX:       print string on a graphics screen, double width
GPRINT2X:      print string on a graphics screen, double size
GPRINTDOWNX:   print string vertically on graph screen, 2x width
GPRINTDOWN2X:  print string vertically on graph screen, 2x size
GPRINTUPX:     print string vertically on graph screen, 2x width
GPRINTUP2X:    print string vertically on graph screen, 2x size
Source:        gprintx.asm ($graph.asm, f8x14.asm, $gp00.asm, $gp02.asm,
                            $gp06.asm, $gp08.asm, $gp10.asm, others)


               Variations of GPrint and GPrintDOWN/GPrintUP;
               GPrintx, GPrintDOWNx and GPrintUPx print characters
               which are twice as wide as normal; 2x subroutines
               print the characters twice as wide and twice as high
               as normal.

               Parameters, supported modes and drawmodes are same as
               GPrint.  GPrintx and GPrint2x also work with user-defined
               fonts.  See GPrint.
Example:       see GPrint.



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GPUTCHR:       print a single character on graphics screen
Source:        gputchr.asm (gprint.asm)

Call with:     DS:[DX] pointing to (x,y) coordinate data
               AL = character to print
Returns:       nothing
Uses:          CX
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

public  mycode
extrn   gputchr:proc

.data
xy      dw 10,10        ; (x,y) coordinates for character

.code
mycode  proc
; program fragment assumes screen in graphics mode
        .
        .
        .
        lea     dx,xy   ; DS:[DX] points to coordinate data
        mov     al,'A'
        call    gputchr
        .
        .
        .
        ret
mycode  endp
        end




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GSAVE:         saves a graphics screen as a disk file
               does not compress image
Source:        gsave.asm ($graph.asm, $gbytes.asm, $reset.asm)

Call with:     DS:[DX] pointing to ASCIIZ filename
               disk space requirements vary depending on graphics mode:

                 HGraph  (mono)       32,768 bytes
                 HGraph  (InColor)   131,072 bytes
                 VGA13X(0)            64,000 bytes
                 VGA13X(1)            76,800 bytes
                 VGA13X(2)           128,000 bytes
                 VGA13X(3)           172,800 bytes
                 XMode16  varies; up to 240,000 bytes
                 VESA6Ah, SVGA16(0)  240,000 bytes
                 SVGA16(1)           393,216 bytes
                 SVGA256(0)          256,000 bytes
                 SVGA256(1)          307,200 bytes
                 SVGA256(2)          480,000 bytes
                 SVGA256(3)          786,432 bytes
                 04h/05h/06h          16,384 bytes
                 40h                  32,768 bytes
                 0Dh                  32,000 bytes
                 0Eh                  64,000 bytes
                 0Fh                  56,000 bytes
                 10h                 112,000 bytes
                 11h                  38,400 bytes
                 12h                 153,600 bytes
                 13h                  64,000 bytes

Returns:       if AX <> 0, AX = MS-DOS error code
               if AX = 0, no error
Uses:          AX, flags
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   gsave:proc

.data
filename db 'graph.bin',0

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea   dx,filename         ; point to ASCIIZ filename
        call  gsave               ; save graph
        or    ax,ax               ; was there a problem?
        jnz   oops                ; do some error control if so


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GSAVEEMS:      copies the graphics screen buffer to EMS memory; does not
               compress the image
Source:        gsaveems.asm ($graph.asm, ems.asm, $gbytes.asm, $emspage.asm
                             banks.asm, $reset.asm, emputget.asm, $plane.asm
                             $gsavex.asm)

Call with:     no parameters; you should use IsEMS before calling this
               subroutine to determine if EMS memory is installed.  Memory
               required is tha same as for GSave, above.
Returns:       if CF = 0, BX = EMS handle
               if CF = 1, AH = EMS error code
Uses:          AX, BX, flags
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

public  testems
extrn   mode43:proc, getkey:proc, isems:proc, gsaveems:proc, gloadems:proc

.data
handle  dw 0

.code
testems proc
        mov     ax,12h          ; VGA 16-color mode
        int     10h
        .
        .
; program draws screen
        .
        call    isems
        jc      no_ems
        call    gsaveems
        jc      no_ems
        mov     handle,bx
        .
        .
; some time later ...
        mov     bx,handle
        call    gloadems
        jc      kill_ems
        call    getkey
kill_ems:
        mov     dx,handle
        mov     ah,45h          ; EMS function: de-allocate block
        int     67h

no_ems: call    mode43
        ret
testems endp
        end


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GSAVEXMS:      copies the graphics screen buffer to XMS memory; does not
               compress the image
Source:        gsavexms.asm ($graph.asm, xms.asm, $gbytes.asm, $gsavex.asm,
                             banks.asm, $reset.asm, xmputget.asm, $plane.asm)

Call with:     no parameters; you must use IsXMS before calling this
               subroutine to determine if XMS memory is installed.  Memory
               required is tha same as for GSave, above.
Returns:       if CF = 0, BX = XMS handle
               if CF = 1, AH = XMS error code
Uses:          AX, BX, flags
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

public  testxms
extrn   mode43:proc, getkey:proc, isxms:proc, gsaveems:proc, gloadxms:proc
extrn   freexms:proc

.data
handle  dw 0

.code
testxms proc
        mov     ax,12h          ; VGA 16-color mode
        int     10h
        .
        .
; program draws screen
        .
        call    isxms
        jc      no_xms
        call    gsavexms
        jc      no_xms
        mov     handle,bx
        .
        .
; some time later ...
        mov     bx,handle
        call    gloadxms
        jc      kill_xms
        call    getkey
kill_xms:
        mov     bx,handle
        call    freexms

no_xms: call    mode43
        ret
testxms endp
        end


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

LINEPATTERN:   defines an optional pattern for DrawLine and DrawBox
Source:        lpattern.asm ($graph.asm)

Call with:     DS:[BX] pointing to an ASCIIZ string of up to 8 characters.
               The bit patterns in each character are used to make dashed
               or dotted lines. For drawmodes > 0, each pixel in the line
               is updated with the foreground color if the corresponding
               bit in the bit pattern is 1.  If the bit in the bit pattern
               is 0, the corresponding pixel in the line is treated as a
               background pixel.  LinePattern must be called before each
               call to a subroutine in drawline.obj if you want the line
               pattern to be used.

               drawmodes supported are:
               (monochrome modes)
                2 = update foreground pixels only
                1 = update foreground and background pixels
                0 = XOR the foreground color with the existing image
               -1 = like drawmode 1, but foreground and background colors
                    are reversed
               -2 = like drawmode 2, but foreground and background colors
                    are reversed
               (color modes)
               same as monochrome, plus:
                3 = OR the foreground pixels with the pre-existing screen
               -3 = OR the background pixels with the pre-existing screen
                4 = AND the foreground pixels with the pre-existing screen
               -4 = AND the background pixels with the pre-existing screen

Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   linepattern:proc, drawline:proc

.data
x0      dw 25,10,301,97          ; line endpoints at (25,10) & (301,97)
pattern db 4 dup(32,64),0        ; 8 bytes past x0

.code
; program fragment assumes DS:@data
        .
        .
        lea   bx,pattern         ; DS:[BX] points to bit pattern
        call  linepattern        ; let drawline know what pattern to use
        sub   bx,8               ; point to line endpoint data
        call  drawline           ; draw a patterned line


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

LOADPCX:       reads a .PCX-format file from disk and unpacks to screen
Source:        loadpcx.asm ($graph.asm, allocdos.asm, color16.asm,
                            fopen.asm, fseek.asm, fget.asm, fgetchr.asm,
                            $plane.asm, $reset.asm)

Call with:     DS:[DX] pointing to ASCIIZ filename of .PCX file
               LoadPCX assumes that the video system is in an appropriate
               mode for the image; see PCXInfo (GRAPHICS.DOC).
               The dimensions of the image in the .PCX file need not
               match the screen dimensions exactly; any 16-color image
               may be loaded to a 16-color screen (up to 800 x 600); if
               the image is too large for the video buffer, either the
               upper left portion of the image is unpacked, or you may
               re-size the video buffer (see BufferDim) to fit the image.
               Any 2-color ("monochrome") image may be loaded to any
               monochrome screen.

               256-color PCX files intended for the standard 320x200
               mode 13h may be loaded to the non-standard VGA13X modes.
               In VGA13X modes with 400 or 480 vertical pixel rows,
               a 320x200 image is stretched to fit image proportions.
Returns:       if CF = 0, no error
               if CF = 1, AX = DOS error code
Uses:          AX, flags
Supports:      All ASMLIB graphics modes EXCEPT:
                  InColor (palette not working right)
                  mode 04h, 05h (no palette)
                  mode 0Fh (EGA monochrome)
Example:       see PCXInfo and BufferDim         
               



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

PUTBITBLOCK:   restores bit block saved by GetBitBlock
PUTBITPLANE:   restores bit plane saved by GetBitPlane
Source:        same as GetBitBlock or GetBitPlane

Call with:     DS:[BX] pointing to upper left corner coordinates
               ES:[DI] pointing to buffer with stored bit block
                PutBitPlane: AL = plane number
                valid plane numbers for 16-color modes are 0 - 3
                                    for EGA mode 11h       0 & 2

               Drawmodes supported are:
                mode 13h, VGA13x, SVGA256:
                 1 = replace existing screen area with bit block
                 2 = replace existing screen with non-zero pixels
                     in bit block

                HGraph (InColor):
                 4 = AND the bit block with the existing screen
                 3 = OR the bit block with the existing screen
                 1,2 = replace existing screen area with bit block
                 0 = XOR the bit block with the existing image
                -1,-2 = replace existing screen area with inverse bit block

                16-color EGA/VGA-type modes and mode 0Fh:
                 same as InColor, plus:
                -3 = OR the inverse bit block with the existing screen
                -4 = AND the inverse bit block with the existing screen

                mode 04h, 05h, 06h, 40h, HGraph (mono), 11h:
                 4, 1, 0, -1 same as InColor
                 2, 3 = combine non-zero pixels in the bit block with the
                        pre-existing image
                -2 = combine non-zero pixel in the inverse bit block with
                     the pre-existing screen image

               Most PutBitBlock code ignores View limits (see GetView)
               but BB08.ASM, BB10.ASM and BB14.ASM (for 256-color modes)
               will clip bitblocks at View boundaries.

Returns:       nothing
Uses:          nothing
Supports:      all ASMLIB graphics modes
Example:       see GetBitBlock


bit block formats explained on following pages



; BIT BLOCK FORMATS

; mode 04h, 05h, 06h Hercules monochrome, 11h, and bit planes
;
; the first word in the buffer is the number of pixel rows (vertical)
; in the bit block; the second word is the number of bytes per screen row;
; the fifth byte is a bit mask for the last byte of each pixel row.
; The bit mask = 0FFh for byte-aligned bit blocks.

bblock  dw 15,5              ; 15 rows, 5 bytes per row
        db 11111110b         ; bit mask for right end of pixel row
                             ; bit block data follows:
                             ;  15 rows, 5 bytes per row
        db 00000000b,10000000b,00000000b,10000000b,00000010b
        db 00000001b,11000000b,00000001b,11000000b,00000110b
        db 00000011b,11100000b,00000011b,11100000b,00001100b
        db 00000111b,01110000b,00000111b,01110000b,00011000b
        db 00001110b,00111000b,00001110b,00111000b,00110000b
        db 00011100b,00011100b,00011100b,00011100b,01100000b
        db 00000001b,11000000b,00000001b,11000000b,11000000b
        db 00000001b,11000000b,00000001b,11000000b,01100000b
        db 00000001b,11000000b,00000001b,11000000b,00110000b
        db 00000001b,11000000b,00000001b,11000000b,00011000b
        db 00000001b,11000000b,00000001b,11000000b,00001100b
        db 00000001b,11000000b,00000001b,11000000b,00000110b
        db 00000001b,11000000b,00000001b,11000000b,00000010b
        db 00000001b,11000000b,00000001b,11000000b,00000000b
        db 00000001b,11000000b,00000001b,11000000b,00000000b

; 16-color modes: 0Dh, 0Eh, 10h, 12h, 6Ah, xmode16, InColor:
; same as above, except there are 4 planes of bit block data
; i. e., 4 groups of 15-row, 5-byte data; plane 3 is the first
; block, followed by planes 2, 1, and 0.

; EGA monochrome mode: 0Fh
; similar to 16-color modes, but there are only 2 groups of bit
; block data instead of 4


; 256-color modes on next page



; BIT BLOCK FORMATS

; mode 13h: no bit mask in the bit block header

red     equ 12                    ; bright red
blue    equ 1                     ; blue

bblock  dw 12,5                   ; 12 rows, 5 bytes per row
        db red, red, blue,red, red
        db red, blue,red, blue,red
        db blue,red, red, red, blue
        db red, red, blue,red, red
        db red, blue,red, blue,red
        db blue,red, red, red, blue
        db red, red, blue,red, red
        db red, blue,red, blue,red
        db blue,red, red, red, blue
        db red, red, blue,red, red
        db red, blue,red, blue,red
        db blue,red, red, red, blue

; vga13x: no bit mask in the bit block header, x & y
; orienation of data is reversed for speed
; this example is the same pattern shown for mode 13h, above

red     equ 12                    ; bright red
blue    equ 1                     ; blue

bblock  dw 12,5                   ; 12 rows, 5 bytes per row
        db red, red, blue,red, red, blue,red, red, blue,red, red, blue
        db red, blue,red, red, blue,red, red, blue,red, red, blue,red
        db blue,red, red, blue,red, red, blue,red, red, blue,red, red
        db red, blue,red, red, blue,red, red, blue,red, red, blue,red
        db red, red, blue,red, red, blue,red, red, blue,red, red, blue



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

PUTDOT:        change a pixel on a graphics screen
Source:        putdot.asm ($graph.asm, $putdot.asm, others)

Call with:     DS:[BX] pointing to x & y coordinates
               Drawmodes supported are:
               (monochrome)
                1 = set pixel
                0 = toggle pixel
               -1 = erase pixel

               (color modes)
                3 = OR foreground color with pre-existing pixel
                1, 2 = replace pixel with foreground color
                0 = XOR foreground color with pre-existing pixel
               -1, -2 = replace pixel with background color
               -3 = OR background color with pre-existing pixel
Returns:       if CF = 0, no error
               if CF = 1, pixel coordinates outside active view area
Uses:          CF; all other registers and flags are saved
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   putdot:proc

.data
extrn   drawmode:byte
x       dw 100,117            ; pixel at x = 100, y = 117

.code
; program fragment assumes DS:@data
        .
        .
        .
        mov   drawmode,1      ; use foreground color
        lea   bx,x            ; point to pixel coordinates
        call  putdot




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

PCXINFO:       read vital information from .PCX-format graphics file
Source:        pcxinfo.asm

Call with:     DS:[DX] pointing to ASCIIZ name of .PCX file
Returns:       DS:[BX] pointing to PCX information data structure:

               pcx_info struc
               horiz    dw 0
               vert     dw 0
               colors   dw 0
               planes   db 0
               xpixels  dw 0
               ypixels  dw 0
               pcx_info ends

               horiz and vert are screen dimensions
               colors: 16 for EGA/VGA 16-color modes, 256 for 256-color modes
               planes: number of pit planes encoded
                       4 for 16-color modes, 1 for monochrome, CGA or mode 13h
               xpixels: horizontal image size
               ypixels: vertical image size




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

RESETVIEW:     restores default view area on active graphics page and
               returns a pointer to the view data
Source:        view.asm ($graph.asm)

Call with:     no parameters
               ResetView restores the default full screen view area.
               The far pointer returned points to ASMLIB's data area in
               $graph.obj for the active graphics page's view coordinates.
Returns:       ES:[BX] pointing to the active page's view data.
Uses:          ES, BX; all other registers and flags are saved
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   resetview:proc

x0 EQU word ptr ES:[BX]
y0 EQU word ptr ES:2[BX]
x1 EQU word ptr ES:4[BX]
y1 EQU word ptr ES:6[BX]

.code
        .
        .
        .
        call  resetview




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SCREENORIGIN:  control position of re-sized video buffer on screen
               see also BufferDim in GRAPHICS.DOC
Source:        scrnorig.asm

Call with:     DS:[BX] pointing to upper-left coordinates of logical
               video buffer to be displayed at upper-left corner of screen.
Returns:       nothing
Uses:          nothing
Supports:      EGA/VGA 16-color modes re-sized with BufferDim
Example:       see BufferDim


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SHOWGPAGE:     change graphics page displayed on screen
               See also UseGPage and GPage.
Source:        gpage1.asm ($graph.asm, $herc.asm)

Call with:     BL = page number
Returns:       Carry Flag = error code
               if CF = 0, no error
               if CF = 1, bad page number
Uses:          CF
Supports:      HGraph (mono and InColor), modes 0Dh, 0Eh, 0Fh, 10h, VGA13X
Example:

include asm.inc

extrn   showgpage:proc

.code
        .
        .
        .
        mov   bl,1           ; show page 1
        call  showgpage
        jc    no_page_1      ; no page 1 for this mode


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SHOWGPLANE:    show one or more planes of multi-plane EGA/VGA screen
Source:        gplane.asm ($graph.asm)

Call with:     AL = plane mask
               Bits set in the plane mask correspond to the plane displayed.
               ASMLIB's default mask is 00001111b, enabling all 4 planes.
Returns:       CF = error flag
               if CF = 0, no error
               if CF = 1, bad plane mask or graphics mode
Uses:          CF
Supports:      EGA & VGA 16-color modes, including VESA 6Ah, xmode16
                   and SVGA16
               EGA monochrome: planes 0 and 2
                   (mask = 00000101b for both planes)
               Hercules InColor
Example:

include asm.inc

extrn   showgplane:proc

.code
        .
        .
        .
        mov   al,00000101b      ; show planes 0 and 2
        call  showgplane
        jc    error             ; error control




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SMALLTEXT:     change GPrint, GPrintX and GPrint2X default to 8x8 characters
               in Hercules and modes 10h, 11h, 12h; makes 8x8-size
               high ASCII characters available to GPrint in all modes
Source:        smalltxt.asm (f8x8.asm, $graph.asm)

STDTEXT:       restore GPrint default characters (see GPrint)
Source:        stdtext.asm (f8x14.asm, fontdata.asm)

Call with:     no parameters
Returns:       nothing
Uses:          nothing; all registers and flags are saved
Example:

include asm.inc

extrn   smalltext:proc, stdtext:proc

.code
        .
        .
        .
; make GPrint use the small 8x8 characters
; make sure high ASCII characters are available
        call   smalltext
        .
        .

; sometime later, I want to use larger 8x14 characters
        call   stdtext



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

UC2SYS:        convert user-defined coordinates to system coordinates
Source:        uc2sys.asm ($graph.asm)

Call with:     DS:[BX] pointing to (x0,y0,x1,y1) coordinates in
               user-defined format
               assumes DS:@data
Returns:       DS:[BX] pointing to (x0,y0,x1,y1) coordinates in system
               format
               UCINIT and UC2SYS allow the programmer to define a
               graph coordinate system to fit the data, and converts
               the system's y-orientation from top-to-bottom to the more
               familiar bottom-to-top
               US2SYS maintains a separate data area for converted
               coordinates; the input coordinates are not changed
Uses:          BX
Supports:      all ASMLIB graphics modes; user-defined coordinates
               from -32767 to +32767; see also UCINIT
Example:       see UCINIT



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

UCINIT:        specify user-defined coordinates
Source:        uc2sys.asm ($graph.asm)

Call with:     DS:[BX] pointing to desired xmin, ymin, xmax, ymax
               coordinates (xmax-xmin < 32767, ymax-ymin < 32767)
               assumes DS:@data
               ASMLIB's default user coordinates are (0,0,1000,1000)
Returns:       nothing
Uses:          nothing
Example:

; I'm plotting a graph on the screen with x-axis data from 1983 to 2007
; and y-axis data from -72 to 140
; I'll leave some space on each side for titles, etc.

extrn   ucinit:proc, uc2sys:proc
extrn   drawbox:proc

.data
x0      dw 1975    ; xmin
y0      dw -80     ; ymin
x1      dw 2014    ; xmax
y1      dw 148     ; ymax

.code
; program fragment assumes DS:@data
        .
        .
        .
; establish coordinates
        lea     bx,x0
        call    ucinit

; draw a box arouund the graph
        mov     x0,1983
        mov     y0,-72
        mov     x1,2007
        mov     y1,140
        lea     bx,x0
        call    uc2sys
        call    drawbox

; SEE ALSO BARGRAPH.ASM EXAMPLE PROGRAM



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

USEGPAGE:      changes active graphics page used by ASMLIB
               does not change page displayed (see GPage and ShowGPage)
Source:        gpage.asm ($graph.asm, $herc.asm)

Call with:     BL = page number
Returns:       if CF = 0, no error
               if CF = 1, bad page number
Uses:          CF
Supports:      HGraph (mono and InColor) with Use64k
               EGA and VGA: modes with more than one page
Example:

include asm.inc

extrn   usegpage:proc

.code
        .
        .
        mov   bl,1
        call  usegpage
        jc    oops



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VIEWLIMIT:     determine current mode's maximum dimensions
Source:        view.asm ($graph.asm)

Call with:     no parameters
Returns:       ES:[BX] pointing to xmax
               ES:2[BX] pointing to ymax
Uses:          ES, BX
Supports:      all ASMLIB graphics modes
Example:

include asm.inc

extrn   viewlimit:proc

.code
        .
        .
        call  viewlimit