HELP FILE ON C-- INLINE ASSEMBLY (Last modifed 29 Dec 1993)
         ^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^

C-- inline assembly supports all of the 8088/8086 assembly codes, plus most
of the 80286 and 80386 enhanced instructions.  All codes must start with the
$ inline assembly specifier.  The list below shows all of the assembly op
codes supported by C--:

$CS:         /* Use Code Segment */
$DS:         /* Use Data Segment */
$ES:         /* Use Extra Segment */
$FS:         /* Use Extra Segment 2 (386+) */
$GS:         /* Use Extra Segment 3 (386+) */
$SS:         /* Use Stack Segment */

$AAA         /* ASCII Adjust After Addition */
$AAD         /* ASCII Adjust After Division */
$AAM         /* ASCII Adjust After Multiplication */
$AAS         /* ASCII Adjust After Subtraction */

$ADC wordreg,value16    /* Add with carry value16 to wordreg */
$ADC bytereg,value8     /* Add with carry value8 to bytereg */
$ADC var16,imm16        /* Add with carry imm16 to 16 bit variable */
$ADC var16,wordreg      /* Add with carry wordreg to 16 bit variable */
$ADC var8,imm8          /* Add with carry imm8 to 8 bit variable */
$ADC var8,bytereg       /* Add with carry bytereg to 8 bit variable */ 

$ADD wordreg,value16    /* Add value16 to wordreg */
$ADD bytereg,value8     /* Add value8 to bytereg */
$ADD var8,imm8          /* Add imm8 to 8 bit variable */
$ADD var8,bytereg       /* Add bytereg to 8 bit variable */ 
$ADD var16,imm16        /* Add imm16 to 16 bit variable */
$ADD var16,wordreg      /* Add wordreg to 16 bit variable */

$ADRSIZ     /* toggle address size (386+) */
$ADRSIZE    /* toggle address size (386+) same as $ADRSIZ */

$AND wordreg,value16    /* And value16 to wordreg */
$AND bytereg,value8     /* And value8 to bytereg */
$AND var8,imm8          /* And imm8 to 8 bit variable */
$AND var8,bytereg       /* And bytereg to 8 bit variable */ 
$AND var16,imm16        /* And imm16 to 16 bit variable */
$AND var16,wordreg      /* And wordreg to 16 bit variable */

$BOUND reg16,var        /* Check Bounds */

$CALL imm16             /* Near Call */
$CALL FAR imm16:imm16   /* Far Call */
$CALL wordreg           /* CALL Near Address In Word Register */
$CALL var               /* Indirect Near Call */
$CALL FAR var           /* Indirect Far Call

$CBD         /* Convert Byte To Double Word (386+), AL to EAX */
$CBW         /* Convert Byte To Word, AL to AX */
$CDQ         /* Convert Double Word To Quad Word (386+), EAX to EDX:EAX */
$CLC         /* Clear Carry Flag */
$CLD         /* Clear Direction Flag */
$CLI         /* Clear Interrupt Flag (disable interrupts) */
$CLTS        /* Clear Task Switched Flag (286+) */
$CMC         /* Complement Carry Flag */
$CWD         /* Convert Word To Double Word, AX to DX:AX */

$CMP bytereg,value8     /* Compare value8 to bytereg */
$CMP wordreg,value16    /* Compare value16 to wordreg */
$CMP var8,imm8          /* Compare imm8 to 8 bit variable */
$CMP var8,bytereg       /* Compare bytereg to 8 bit variable */ 
$CMP var16,imm16        /* Compare imm16 to 16 bit variable */
$CMP var16,wordreg      /* Compare wordreg to 16 bit variable */

$CMPSB       /* Compare String Byte */
$CMPSW       /* Compare String Word */
$CMPSD       /* Compare String Double Word (386+) */

$DAA         /* Decimal Adjust After Addition */
$DAS         /* Decimal Adjust After Subtraction */

$DB imm8     /* Data Byte (a method for putting a byte value in code) */
$DW imm16    /* Data Word (a method for putting a word value in code) */

$DEC varreg8   /* Decrement an 8 bit memory variable or register */
$DEC varreg16  /* Decrement a 16 bit memory variable or register */
$DEC varreg32  /* Decrement a 32 bit memory variable or register (386+) */

$DIV varreg8   /* Divide AX by an 8 bit memory var or register */
$DIV varreg16  /* Divide DX-AX by a 16 bit memory var or register */
$DIV varreg32  /* Divide EDX-EAX by a 32 bit memory var or register (386+) */

$ENTER imm16,imm8   /* Make Stack Frame (286+) */

$HLT         /* Halt Processor */

$IDIV varreg8   /* Integer Divide AL by an 8 bit memory var or register */
$IDIV varreg16  /* Integer Divide AX by a 16 bit memory var or register */
$IDIV varreg32  /* Integer Divide EAX by a 32 bit memory var or reg (386+) */

$IMUL varreg8   /* Integer Multiply AL by an 8 bit memory var or register */
$IMUL varreg16  /* Integer Multiply AX by a 16 bit memory var or register */
$IMUL varreg32  /* Integer Multiply EAX by a 32 bit mem var or reg (386+) */

$IN AL,imm8   /* Read A Byte Into AL From A Constant Port Number */
$IN AX,imm8   /* Read A Word Into AX From A Constant Port Number */
$IN EAX,imm8  /* Read A Word Into EAX From A Constant Port Number (386+) */
$IN AL,DX     /* Read A Byte Into AL From Port DX */
$IN AX,DX     /* Read A Word Into AX From Port DX */
$IN EAX,DX    /* Read A Word Into EAX From Port DX (80386+) */

$INC varreg8   /* Increment an 8 bit memory variable or register */
$INC varreg16  /* Increment a 16 bit memory variable or register */

$INSB        /* Input String Byte (286+) */
$INSW        /* Input String Word (286+) */
$INSD        /* Input String Double Word (386+) */

$INT imm8    /* Call To Interrupt */
$INTO        /* Interrupt 4 On Overflow */

$IRET        /* Return From Interrupt */

$JMP SHORT imm8        /* Direct Short Jump */
$JMP imm16             /* Direct Near Jump */
$JMP FAR imm16:imm16   /* Direct Far Jump */
$JMP wordreg           /* Jump To Near Address In Word Register */
$JMP var16             /* Indirect Near Jump */
$JMP FAR var           /* Indirect Far Jump */
$JMP var32             /* Indirect Far Jump */

$JNO imm8        /* Jump Short On Not Overflow */
$JNO imm16       /* Jump Near On Not Overflow (386+) */

$JO imm8         /* Jump Short On Overflow */
$JO imm16        /* Jump Near On Overflow (386+) */

$JB imm8         /* Jump Short On Below */
$JB imm16        /* Jump Near On Below (386+) */

$JNAE imm8       /* Jump Short On Not Above Or Equal */
$JNAE imm16      /* Jump Near On Not Above Or Equal (386+) */

$JNB imm8        /* Jump Short On Not Below */
$JNB imm16       /* Jump Near On Not Below (386+) */

$JAE imm8        /* Jump Short On Above Or Equal */
$JAE imm16       /* Jump Near On Above Or Equal (386+) */

$JE imm8         /* Jump Short On Equal */
$JE imm16        /* Jump Near On Equal (386+) */

$JZ imm8         /* Jump Short On Zero */
$JZ imm16        /* Jump Near On Zero (386+) */

$JNE imm8        /* Jump Short On Not Equal */
$JNE imm16       /* Jump Near On Not Equal (386+) */

$JNZ imm8        /* Jump Short On Not Zero */
$JNZ imm16       /* Jump Near On Not Zero (386+) */

$JBE imm8        /* Jump Short On Below Or Equal */
$JBE imm16       /* Jump Near On Below Or Equal (386+) */

$JNA imm8        /* Jump Short On Not Above */
$JNA imm16       /* Jump Near On Not Above (386+) */

$JNBE imm8       /* Jump Short On Not Below Or Equal */
$JNBE imm16      /* Jump Near On Not Below Or Equal (386+) */

$JA imm8         /* Jump Short On Above */
$JA imm16        /* Jump Near On Above (386+) */

$JS imm8         /* Jump Short On Sign */
$JS imm16        /* Jump Near On Sign (386+) */

$JNS imm8        /* Jump Short On Not Sign */
$JNS imm16       /* Jump Near On Not Sign (386+) */

$JP imm8         /* Jump Short On Parity */
$JP imm16        /* Jump Near On Parity (386+) */

$JPE imm8        /* Jump Short On Parity Even */
$JPE imm16       /* Jump Near On Parity Even (386+) */

$JNP imm8        /* Jump Short On Not Parity */
$JNP imm16       /* Jump Near On Not Parity (386+) */

$JPO imm8        /* Jump Short On Parity Odd */
$JPO imm16       /* Jump Near On Parity Odd (386+) */

$JL imm8         /* Jump Short On Less */
$JL imm16        /* Jump Near On Less (386+) */

$JNGE imm8       /* Jump Short On Not Greater Or Equal */
$JNGE imm16      /* Jump Near On Not Greater Or Equal (386+) */

$JNL imm8        /* Jump Short On Not Less */
$JNL imm16       /* Jump Near On Not Less (386+) */

$JGE imm8        /* Jump Short On Greater Or Equal */
$JGE imm16       /* Jump Near On Greater Or Equal (386+) */

$JLE imm8        /* Jump Short On Less Or Equal */
$JLE imm16       /* Jump Near On Less Or Equal (386+) */

$JNG imm8        /* Jump Short On Not Greater */
$JNG imm16       /* Jump Near On Not Greater (386+) */

$JNLE imm8       /* Jump Short On Not Less Or Equal */
$JNLE imm16      /* Jump Near On Not Less Or Equal (386+) */

$JG imm8         /* Jump Short On Greater */
$JG imm16        /* Jump Near On Greater (386+) */

$JCXZ imm8       /* Jump Short On CX == 0 */
$JCXZ imm16      /* Jump Near On CX == 0 (386+) */

$LAHF        /* Load Flags Into AH Register */

$LDS reg16,var     /* Load DS pointer */
$LEA reg16,var     /* Load Effective Address */

$LEAVE       /* Release Stack Frame (286+) */

$LES reg16,var     /* Load ES pointer */
$LFS reg16,var     /* Load FS pointer (386+) */
$LGS reg16,var     /* Load GS pointer (386+) */

$LODSB     /* Load String Byte:  AL = DSBYTE[DI]; DI++; */
$LODSW     /* Load String Word:  AX = DSWORD[DI]; DI+=2; */
$LODSD     /* Load String Double Word (386+):  EAX = DSDWORD[DI]; DI+=4; */

$LOCK      /* Bus Lock */

$LOOP imm8       /* Loop CX Times */
$LOOPE imm8      /* Loop CX Times While Equal */
$LOOPNE imm8     /* Loop CX Times While Not Equal */
$LOOPNZ imm8     /* Loop CX Times While Not Zero */
$LOOPZ imm8      /* Loop CX Times While Zero */

$LSS reg16,var     /* Load SS pointer (386+) */

$MOV wordreg,value16   /* move value16 into word register */
$MOV bytereg,value8    /* move value8 into byte register */
$MOV var16,wordreg     /* move word register into 16 bit variable */
$MOV var8,bytereg      /* move byte register into 8 bit variable */
$MOV var16,imm16       /* move constant value into 16 bit variable */
$MOV var8,imm8         /* move constant value into 8 bit variable */
$MOV var16,segreg      /* move segment register into 16 bit variable */
$MOV wordreg,segreg    /* move segment register into word register */
$MOV var16,seg386      /* move 386 seg reg into 16 bit var (386+) */
$MOV wordreg,seg386    /* move 386 seg reg into word reg (386+) */
$MOV wordreg,imm16     /* move constant value into word register */
$MOV bytereg,imm8      /* move constant value into byte register */
$MOV segreg,var16      /* move word variable into segment register */
$MOV segreg,wordreg    /* move word reg into segment register */
$MOV seg386,var16      /* move word variable into 386 seg reg (386+) */
$MOV seg386,wordreg    /* move word register into 386 seg reg (386+) */
$MOV reg32,reg32       /* move 32 bit reg into 32 bit reg (386+) */
$MOV reg32,debugreg    /* move debug reg into 32 bit reg (386+) */
$MOV reg32,testreg     /* move test reg into 32 bit reg (386+) */
$MOV reg32,controlreg  /* move control reg into 32 bit reg (386+) */
$MOV debugreg,reg32    /* move 32 bit reg into debug reg (386+) */
$MOV testreg,reg32     /* move 32 bit reg into test reg (386+) */
$MOV controlreg,reg32  /* move 32 bit reg into control reg (386+) */

$MOVSB       /* Move String Byte: ESBYTE[DI] = DSBYTE[SI]; DI++; SI++; */
$MOVSW       /* Move String Word: ESWORD[DI] = DSWORD[SI]; DI+=2; SI+=2; */
$MOVSD       /* Move String Double Word (80386+):
                                 ESDWORD[DI] = DSDWORD[SI]; DI+=4; SI+=4; */

$MUL varreg8   /* Multiply AL by an 8 bit memory variable or register,
                  result stored in AX */
$MUL varreg16  /* Multiply AX by a 16 bit memory variable or register,
                  high 16 bits of result stored in DX, low 16 bits of
                  result stored in AX */
$MUL varreg32  /* Multiply EAX by a 32 bit memory variable or register,
                  high 32 bits of result stored in EDX, low 32 bits of
                  result stored in EAX (80386+) */

$NEG varreg8   /* Negate an 8 bit memory variable or register */
$NEG varreg16  /* Negate a 16 bit memory variable or register */

$NOP         /* No Operation */

$NOT varreg8   /* Not an 8 bit memory variable or register */
$NOT varreg16  /* Not a 16 bit memory variable or register */

$OPSIZ     /* toggle operand size (386+) */
$OPSIZE    /* toggle operand size (386+) */

$OR wordreg,value16    /* Or value16 to wordreg */
$OR bytereg,value8     /* Or value8 to bytereg */
$OR var16,imm16        /* Or imm16 to 16 bit variable */
$OR var16,wordreg      /* Or wordreg to 16 bit variable */
$OR var8,imm8          /* Or imm8 to 8 bit variable */
$OR var8,bytereg       /* Or bytereg to 8 bit variable */ 

$OUT imm8,AL   /* Write AL To A Constant Port Number */
$OUT imm8,AX   /* Write AX To A Constant Port Number */
$OUT imm8,EAX  /* Write EAX To A Constant Port Number (386+) */
$OUT DX,AL     /* Write AL To Byte Port DX */
$OUT DX,AX     /* Write AX To Word Port DX */
$OUT DX,EAX    /* Write EAX To Word Port DX (386+) */

$OUTSB       /* Output String Byte (286+) */
$OUTSW       /* Output String Word (286+) */
$OUTSD       /* Output String Double Word (386+) */

$POP wordreg  /* POP Word Register Off Stack */
$POP var16    /* POP 16 bit Variable Off Stack */
$POP reg32    /* POP 32 bit Word Register Off Stack (386+) */
$POP segreg   /* POP Segment Register Off Stack */
$POP seg386   /* POP 386 Segment Register (FS or GS) Off Stack (386+) */
$POPA         /* POPs all wordreg registers off stack (286+) */
$POPAD        /* POPs all reg32 registers off stack (386+) */
$POPF         /* POP Flags Off Stack */
$POPFD        /* POP 32 bit Flags Off Stack */

$PUSH wordreg  /* PUSH Word Register Onto Stack */
$PUSH var16    /* PUSH 16 bit Variable Onto Stack */
$PUSH reg32    /* PUSH 32 bit Word Register Onto Stack (386+) */
$PUSH segreg   /* PUSH Segment Register Onto Stack */
$PUSH seg386   /* PUSH 386 Segment Register (FS or GS) Onto Stack (386+) */
$POPA          /* PUSHes all wordreg registers onto stack (286+) */
$POPAD         /* PUSHes all reg32 registers onto stack (386+) */
$PUSHF         /* PUSH Flags Onto Stack */
$PUSHFD        /* PUSH 32 bit Flags Onto Stack (386+) */

$RCL varreg,1      /* Rotate Through Carry Left By One */
$RCL varreg,imm8   /* Rotate Through Carry Left By imm8 (286+) */
$RCL varreg,CL     /* Rotate Through Carry Left By CL */

$RCR varreg,1      /* Rotate Through Carry Right By One */
$RCR varreg,imm8   /* Rotate Through Carry Right By imm8 (286+) */
$RCR varreg,CL     /* Rotate Through Carry Right By CL */

$REPE        /* Repeat While Equal */
$REPZ        /* Repeat While Zero */
$REPNE       /* Repeat While Not Equal */
$REPNZ       /* Repeat While Not Zero */

$RET         /* Near Return */
$RETF        /* Far Return */

$ROL varreg,1      /* Rotate Left By One */
$ROL varreg,imm8   /* Rotate Left By imm8 (286+) */
$ROL varreg,CL     /* Rotate Left By CL */

$ROR varreg,1      /* Rotate Right By One */
$ROR varreg,imm8   /* Rotate Right By imm8 (286+) */
$ROR varreg,CL     /* Rotate Right By CL */

$SAHF        /* Store AH Register Into Flags */

$SAL varreg,1      /* Shift Left Arithmatic By One */
$SAL varreg,imm8   /* Shift Left Arithmatic By imm8 (286+) */
$SAL varreg,CL     /* Shift Left Arithmatic By CL */

$SAR varreg,1      /* Shift Right Arithmatic By One */
$SAR varreg,imm8   /* Shift Right Arithmatic By imm8 (286+) */
$SAR varreg,CL     /* Shift Right Arithmatic By CL */

$SCASB       /* Scan String Byte */
$SCASW       /* Scan String Word */
$SCASD       /* Scan String Double Word (386+) */

$SHL varreg,1      /* Shift Left Logical By One */
$SHL varreg,imm8   /* Shift Left Logical By imm8 (286+) */
$SHL varreg,CL     /* Shift Left Logical By CL */

$SHR varreg,1      /* Shift Right Logical By One */
$SHR varreg,imm8   /* Shift Right Logical By imm8 (286+) */
$SHR varreg,CL     /* Shift Right Logical By CL */

$STC         /* Set Carry Flag */
$STD         /* Set Direction Flag */
$STI         /* Set Interrupt Flag */

$STOSB   /* Store String Byte: ESBYTE[DI] = AL; DI++; */
$STOSW   /* Store String Word: ESWORD[DI] = AX; DI+=2; */
$STOSD   /* Store String Double Word (386+): ESDWORD[DI] = EAX; DI+=4; */

$SBB wordreg,value16    /* Subtract with borrow value16 to wordreg */
$SBB bytereg,value8     /* Subtract with borrow value8 to bytereg */
$SBB var16,imm16        /* Subtract with borrow imm16 to 16 bit variable */
$SBB var16,wordreg      /* Subtract with borrow wordreg to 16 bit variable */
$SBB var8,imm8          /* Subtract with borrow imm8 to 8 bit variable */
$SBB var8,bytereg       /* Subtract with borrow bytereg to 8 bit variable */ 

$SUB wordreg,value16    /* Subtract value16 to wordreg */
$SUB bytereg,value8     /* Subtract value8 to bytereg */
$SUB var16,imm16        /* Subtract imm16 to 16 bit variable */
$SUB var16,wordreg      /* Subtract wordreg to 16 bit variable */
$SUB var8,imm8          /* Subtract imm8 to 8 bit variable */
$SUB var8,bytereg       /* Subtract bytereg to 8 bit variable */ 

$TEST wordreg,value16   /* AND word register and value16 to flags */
$TEST bytereg,value8    /* AND byte register and value16 to flags */

$WAIT        /* Wait For Co-Processor */

$XLAT        /* Table LookUp Translation */
$XLATB       /* Table LookUp Translation (same as XLAT) */

$XOR wordreg,value16    /* Xor value16 to wordreg */
$XOR bytereg,value8     /* Xor value8 to bytereg */
$XOR var16,imm16        /* Xor imm16 to 16 bit variable */
$XOR var16,wordreg      /* Xor wordreg to 16 bit variable */
$XOR var8,imm8          /* Xor imm8 to 8 bit variable */
$XOR var8,bytereg       /* Xor bytereg to 8 bit variable */ 


imm32      represents a 32 bit constant value.
imm16      represents a 16 bit constant value.
imm8       represents an 8 bit constant value.
reg32      represents any one of EAX,EBX,ECX,EDX,ESP,EBP,EDI or ESI.
wordreg    represents any one of AX,BX,CX,DX,SP,BP,DI or SI.
bytereg    represents any one of AL,BL,CL,DL,AH,BH,CH or DH.
segreg     represents any one of DS,CS,ES or SS.
seg386     represents one of the two extra 80386 segments registers, FS or GS.
testreg    represents any one of TR0,TR1,TR2,TR3,TR4,TR5,TR6 or TR7.
debugreg   represents any one of DR0,DR1,DR2,DR3,DR4,DR5,DR6 or DR7.
controlreg represents any one of CR0,CR1,CR2,CR3,CR4,CR5,CR6 or CR7.
var        represents any memory variable.
value32    represents any one of dword, long, imm32 or reg32.
value16    represents any one of word, int, imm16 or wordreg.
value8     represents any one of byte, char, imm8 or bytereg.
varreg32   represents any one of dword, long or reg32.
varreg16   represents any one of word, int or wordreg.
varreg8    represents any one of byte, char or bytereg.
varreg     represents any one of varreg16 or varreg8.
var32      represents a dword or long memory variable
var16      represents a word or int memory variable
var8       represents a byte or char memory variable
(286+)     80286 or higher processor required.
(386+)     80386 or higher processor required.


/* end of C--ASM.DOC */