LIST OF BUILT IN REG AND MACRO FUNCTIONS OF SPHINX C--
^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^
Last Update:  24 Mar 1994


METHOD OF CALLING:  PROCEDURENAME(AX,BX,CX,DX,DI,SI);
			or
        	    @ MACRONAME(AX,BX,CX,DX,DI,SI);

All parameters for REG procedures and MACROS are passed using registers.  The
register used in each position is listed above.

SIZE refers to size of the MACRO, add one byte to the size for REG procedure.
All registers that are modified are listed.


CALLING FORMAT:  ABORT();
DOS REQUIRED:  1.0 +
SIZE:  2 bytes.
FUNCTION:  aborts the program.
RETURNS:  never


CALLING FORMAT:  ADDPIXEL19( ,x,colour,y);
		  colour = colour of pixel desired (0..255)
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  ADDs a pixel to the screen in mode 19 (0x13) graphics mode.
RETURNS:  AX,DX,BX = Undefined.
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  ALLOCBESTFIT();
DOS REQUIRED:  3.0 +
SIZE:  8 bytes.
FUNCTION:  Changes the DOS memory allocation strategy to best fit.
RETURNS:  AX,BX = Undefined.


CALLING FORMAT:  ALLOCFIRSTFIT();
DOS REQUIRED:  3.0 +
SIZE:  8 bytes.
FUNCTION:  Changes the DOS memory allocation strategy to first fit.
RETURNS:  AX,BX = Undefined.


CALLING FORMAT:  ALLOCLASTFIT();
DOS REQUIRED:  3.0 +
SIZE:  8 bytes.
FUNCTION:  Changes the DOS memory allocation strategy to last fit.
RETURNS:  AX,BX = Undefined.


CALLING FORMAT:  ALLOCBESTFIT();
DOS REQUIRED:  3.0 +
SIZE:  8 bytes.
FUNCTION:  Changes the DOS memory allocation strategy to best fit.
RETURNS:  AX,BX = Undefined.


CALLING FORMAT:  ALLOCSTRATEGY();
DOS REQUIRED:  3.0 +
SIZE:  8 bytes.
FUNCTION:  Returns the current DOS memory allocation strategy.
RETURNS:  BX = Undefined.
          AX == 0 if First Fit
             == 1 if Best Fit
             >= 2 if Last Fit


CALLING FORMAT:  ANDPIXEL19( ,x,colour,y);
		  colour = colour of pixel desired (0..255)
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  ANDs a pixel to the screen in mode 19 (0x13) graphics mode.
RETURNS:  AX,DX,BX = Undefined.
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  BASIC();
SIZE:  2 bytes.
FUNCTION:  calls ROM BASIC by interrupt 0x18.
RETURNS:  nothing.


CALLING FORMAT:  BEEP();
DEFINED IN:  WRITE.H--
SIZE:  7 bytes.
FUNCTION:  Emmits the normal IBM beep from the internal speaker using a BIOS
           interrupt.
RETURNS:  AX = undefined
	  BX = 0


CALLING FORMAT:  BIOSEKEYCHECK();
DEFINED IN:  KEYCODES.H--
SIZE:  8 bytes.
FUNCTION:  Checks if a key is available to be read from the enhanced keyboard
	   using a BIOS interrupt.  This function will only work with AT
	   enhanced keyboard BIOS or higher.  This functions will recognize
	   F11 and F12, BIOSKEYCHECK will not.
RETURNS:  If key waiting:
	      AX = key code (AH = keyboard scancode, AL = ASCII character).
	  If no key waiting:
	      AX = 0


CALLING FORMAT:  BIOSEREADKEY();
DEFINED IN:  KEYCODES.H--
SIZE:  4 bytes.
FUNCTION:  Reads a key from the enhanced keyboard using a BIOS interrupt.
	   If no key is waiting to be read from the keyboard buffer, this
	   procedure will wait until a key is pressed.  This function will
	   only work with AT enhanced keyboard BIOS or higher.  This
	   functions will recognize F11 and F12.
RETURNS:  AX = key code (AH = keyboard scancode, AL = ASCII character).


CALLING FORMAT:  BIOSKEYCHECK();
DEFINED IN:  KEYCODES.H--
SIZE:  8 bytes.
FUNCTION:  Checks if a key is available to be read from the enhanced keyboard
	   using a BIOS interrupt.  This functions will not recognize F11 and
	   F12.
RETURNS:  If key waiting:
	      AX = key code (AH = keyboard scancode, AL = ASCII character).
	  If no key waiting:
	      AX = 0


CALLING FORMAT:  BIOSPUSHKEY(keycode);
		  keycode = (AH = keyboard scancode, AL = ASCII character).
DEFINED IN:  KEYCODES.H--
SIZE:  4 bytes.
FUNCTION:  Pushes a key code onto the keyboard buffer using a BIOS interrupt.
	   This function requires AT or higher BIOS.
RETURNS:  AH = 5.


CALLING FORMAT:  BIOSREADKEY();
DEFINED IN:  KEYCODES.H--
SIZE:  4 bytes.
FUNCTION:  Reads a key from the keyboard using a BIOS interrupt.  If no key
	   is waiting to be read from the keyboard buffer, this procedure
	   will wait until a key is pressed.  This function will not
	   recognize F11 and F12.
RETURNS:  AX = key code (AH = keyboard scancode, AL = ASCII character).


CALLING FORMAT:  BIOSSHIFT();
DEFINED IN:  KEYCODES.H--
SIZE:  4 bytes.
FUNCTION:  Reads the status of the shift like keys using a BIOS interrupt.
RETURNS:  AH = 2
	  AL = bit 0 set if right shift key down
	       bit 1 set if left shift key down
	       bit 2 set if Ctrl key down
	       bit 3 set if Alt key down
	       bit 4 set if Scroll Lock On
	       bit 5 set if Num Lock On
	       bit 6 set if Caps Lock On
	       bit 7 set if Insert On


CALLING FORMAT:  BLANKVGA();
SIZE:  6 bytes.
FUNCTION:  Blanks the screen on any VGA display in any mode.  This is done
	   by setting the DAC mask register to 0.  This operation can be
	   undone by calling UNBLANKVGA(), very handy for screen savers.
RETURNS:  AL = 0
	  DX = 0x3C6


CALLING FORMAT:  BYTETODIGITS(number,stringloc);
		  number = byte to be converted to digits string
		  stringloc = location of string
SIZE:  31 bytes.
FUNCTION:  converts a byte value to 3 decimal digits and a NULL terminating
	   character.
RETURNS:  CX,DX = undefined
	  AX = number % 10


CALLING FORMAT:  CLEARSCREEN0();
		 CLEARSCREEN1();
		 CLEARSCREEN2();
		 CLEARSCREEN3();
SIZE:  15 bytes.
FUNCTION:  clears video page 0 of the specifed screen mode.
RETURNS:  CX = 0
	  ES = 0xB800
	  AX = 0x0700
	  DI = undefined


CALLING FORMAT:  CLEARSCREEN4();
		 CLEARSCREEN5();
		 CLEARSCREEN6();
SIZE:  15 bytes.
FUNCTION:  clears the screen.
RETURNS:  CX = 0
	  ES = 0xB800
	  AX = 0x0000 
	  DI = undefined


CALLING FORMAT:  CLEARSCREEN7();
SIZE:  15 bytes.
FUNCTION:  Clears page 0 in video mode 7.
RETURNS:  CX = 0
	  ES = 0xB000
	  AX = 0x0000 
	  DI = undefined


CALLING FORMAT:  CLEARSCREEN17();
		 CLEARSCREEN19();
SIZE:  15 bytes.
FUNCTION:  clears the screen.
EXAMPLE IN:  C--GDEMO.C--
RETURNS:  CX = 0
	  ES = 0xA000
	  AX = 0x0000 
	  DI = undefined


CALLING FORMAT:  CLEARWINDOW( ,attribute,upperleftloc,lowerrightloc);
		  attribute = attribute to be used for blanked area
		  upperleftloc = CH =Y coordinate + CL =X coordinate of the
				 upper left corner of the window
		  lowerrightloc = DH =Y coordinate + DL =X coordinate of the
				  upper left corner of the window
SIZE:  7 bytes.
FUNCTION:  clears a specified window with given attribute.
RETURNS:  AX = 0x0600
	  BH = attribute


CALLING FORMAT:  CLICKOFF();
SIZE:  5 bytes.
FUNCTION:  Turns off the PCjr interrupt key click (available only with PCjr
	   BIOS).
RETURNS:  AX = 0x0400


CALLING FORMAT:  CLICKON();
SIZE:  5 bytes.
FUNCTION:  Turns on the PCjr interrupt key click (available only with PCjr
	   BIOS).
RETURNS:  AX = 0x0401


CALLING FORMAT:  COLDBOOT();
SIZE:  5 bytes.
FUNCTION:  Cold boots the computer.
RETURNS:  Never Ever


CALLING FORMAT:  DELAY(time);
		  time = amount of time to delay in 1/15.3 second time units.
SIZE:  8 bytes.
FUNCTION:  Delays for a certain interval of time by a call to a BIOS
           interrupt.  This function is only available with AT or higher
           BIOS.
RETURNS:  AX,CX,DX = undefined


CALLING FORMAT:  DISABLE();
SIZE:  1 byte.
FUNCTION:  Executes a CLI instruction to disable external interrupts.
RETURNS:  nothing


CALLING FORMAT:  DOSGETDATE();
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  Obtains the system day of the month, day of the week, month, and 
           year.
RETURNS:  AH = 0x2A
          CX = year (1980 to 2099)
          DH = month (1 to 12)
          DL = day (1 to 31)
          Under DOS 1.1 or later:
          AL = day of week (0 = Sunday, 1 = Monday, ...)  


CALLING FORMAT:  DOSGETTIME();
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  Obtains the time of day from the system real-time clock driver,
           converted to hours, minutes, seconds, and hundredths of seconds.
RETURNS:  AH = 0x2C
          CH = hours (0 to 23)
          CL = minutes (0 to 59)
          DH = seconds (0 to 59)
          DL = hundredths of seconds (0 to 99)


CALLING FORMAT:  DOSINPORT();
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  Reads a character from the serial port.
RETURNS:  AH = 3
          AL = 8-bit data


CALLING FORMAT:  DOSOUTPORT( , , ,databyte);
                  databyte = 8-bit data value to be sent.
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  Outputs a character to the serial port.
RETURNS:  AH = 4


CALLING FORMAT:  DOSWRITESTR(stringloc);
		  stringloc = memory location of '$' terminating string
DOS REQUIRED:  1.0 +
SIZE:  6 bytes.
FUNCTION:  Prints a $ terminating string to the screen using DOS interrupt.
RETURNS:  AH = 9


CALLING FORMAT:  EATKEY();
SIZE:  12 bytes.
FUNCTION:  Signals the keyboard controller that the current scan code has
           been recieved.
RETURNS:  AX = undefined


CALLING FORMAT:  ENABLE();
SIZE:  1 byte.
FUNCTION:  Executes a STI instruction to enable external interrupts.
RETURNS:  nothing


CALLING FORMAT:  EOI();
SIZE:  4 byte.
FUNCTION:  Sends the End Of Interrupt signal to the external interrupt
           controller.  This is done by sending the value 0x20 to port 0x20.
RETURNS:  AL = 0x20


CALLING FORMAT:  EXIT(code);
		  code = return code of program 0 to 255
DOS REQUIRED:  2.0 +
SIZE:  4 bytes.
FUNCTION:  Terminates program with return code.
RETURNS:  never


CALLING FORMAT:  FCLOSE( ,handle);
		  handle = file handle
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Closes a file of the given handle.
RETURNS:  Success:  AX = 0
	  Failed:  AX = error code


CALLING FORMAT:  FCREATE( , ,attribute,filename);
		  attribute = file attribute (bits may be combined but are
                              usually all zero):
                             bit 0:  read-only
                             bit 1:  hidden
                             bit 2:  system
                             bit 3:  volume label
                             bit 4:  must be 0
                             bit 5:  archive
                             bit 6 to 15:  must be 0
		  filename = pointer to null-terminating string
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Creates a file of given filename and attribute and returns a file
	   handle.
RETURNS:  Success:  AX = file handle
	  Failed:  AX = 0


CALLING FORMAT:  FDELETE( , , ,filename);
		  filename = pointer to null-terminating string
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Deletes a file of given filename.
RETURNS:  Success:  AX = 0
	  Failed:  AX = error code


CALLING FORMAT:  FHANDLE( ,handle);
		  handle = handle to be copied
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Copies file handle for use after handle has been closed.
RETURNS:  Success:  AX = new handle
	  Failed:  AX = 0


CALLING FORMAT:  FINDFIRSTFILE( , ,attribute,pathname);
                  attribute = search attribute:
                              bit 0 = read only
                              bit 1 = hidden
                              bit 2 = system
                              bit 3 = volume label
                              bit 4 = directory
                              bit 5 = archive
                              bits 6 to 15 = reserved (0)
		  pathname = pointer to null-terminating pathname string
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Searches the default or specified directory and drive for the
           first matching file.  Wild card characters may be used.
EXAMPLE IN:  REFRESH.C-- and TINYDRAW.C--
RETURNS:  File Not Found:  AX = error code
	  File Found:  AX = 0   And the current DTA will contain the
                  following after the search:
               byte offset:
               0x00 to 0x14 = reserved (0)
               0x15         = attribute of matched file or directory
               0x16 to 0x17 = file time:
                              bits 0x0 to 0x4 = 2 second increments (0-29)
                              bits 0x5 to 0xA = minutes (0-59)
                              bits 0xB to 0xF = hours (0-23)
               0x18 to 0x19 = file date:
                              bits 0x0 to 0x4 = day (1-31)
                              bits 0x5 to 0x8 = month (1-12)
                              bits 0x9 to 0xF = year (relative to 1980)
               0x1A to 0x1D = file size
               0x1E to 0x2A = ASCII filename and extension
NOTE:  The initial address of the DTA (Disk Transfer Area) in COM files
       is at the offset 0x80, which is the same address as the location of
       the command line parameters, thus if the DTA is not moved, the
       command line parameters will be lost.


CALLING FORMAT:  FINDNEXTFILE();
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Searches the default or specified directory and drive for the
           next matching file.  FINDFIRSTFILE must be called before using
           this function.
EXAMPLE IN:  TINYDRAW.C--
RETURNS:  File Not Found:  AX = error code
	  File Found:  AX = 0   And the current DTA will contain the
                  same information as for FINDFIRSTFILE, except that it will
                  be the next found file.


CALLING FORMAT:  FOPEN(mode, , ,filename);
		  mode = 0 for read access
			 1 for write access
			 2 for read/write access
		  filename = offset address of filename string
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Opens a file of given filename and attribute and returns a file
	   handle.  A FILE THAT DOES NOT EXIST CANNOT BE OPENED!  Use 
           FCREATE if the file needs to be created.
RETURNS:  Success:  AX = file handle
	  Failed:  AX = 0


CALLING FORMAT:  FREAD( ,handle,count,buffer);
		  handle = file handle
		  count = # of bytes to read
		  buffer = pointer to read buffer
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Reads a number of bytes specified in count from handle into
	   buffer.
RETURNS:  AX = actual # bytes read


CALLING FORMAT:  FWRITE( ,handle,count,buffer);
		  handle = file handle
		  count = # of bytes to write
		  buffer = pointer to write buffer
DOS REQUIRED:  2.0 +
SIZE:  8 bytes.
FUNCTION:  Writes a number of bytes specified in count from buffer into
	   handle.
RETURNS:  AX = actual # bytes written


CALLING FORMAT:  GETBORDERCOLOR();
SIZE:  7 bytes.
FUNCTION:  Calls a BIOS interrupt to get the colour of the border.  This
	   function will only work on VGA or higher graphics cards.
RETURNS:  BH = border colour
	  AH = undefined
	  AL = border colour


CALLING FORMAT:  GETCH();
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  calls DOS interrupt to read a key from the keyboard.
RETURNS:  AH = 8
	  AL = ASCII value of key read


CALLING FORMAT:  GETCHE();
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  calls DOS interrupt to read a key from the keyboard and echo it to
	   the screen.
RETURNS:  AH = 1
	  AL = ASCII value of key read


CALLING FORMAT:  GETCONFIG();
SIZE:  2 bytes.
FUNCTION:  Calls BIOS interrupt 0x11 to get system configuration.
RETURNS:  AX = bit 0 = 1 if floppy drive(s) installed
	       bit 1 = 1 if math coprocessor installed
  	       bit 2 = 1 if pointing device installed (PS/2)
	       bit 3 = don't worry about it
	       bit 4 = don't worry about it
	       bits 4,5 = inital video mode
		        0,0  reserved
		        0,1  40x25 colour text
		        1,0  80x25 colour text
		        1,1  80x25 monochrome text
	       bits 6,7 = number of floppy disk drives
			0,0  1 drive
			0,1  2 drives
			1,0  3 drives
			1,1  4 drives
	       bit 8 = who knows what
	       bits 9,10,11 = number of RS-232 ports installed
	       bit 12 = 1 if game adapter installed
	       bit 13 = don't worry about it
	       bits 14,15 = number of printers installed


CALLING FORMAT:  GETCPU();
SIZE:  83 bytes.
FUNCTION:  Determines whether the system processor is an 8086, 80286, 80386,
           or 80486.
RETURNS:  AH,BX,CX,DX = undefined
          AL = 0 if 8086 or 8088
             = 2 if 80286
             = 3 if 80386
             = 4 if 80486


CALLING FORMAT:  GETDOSVERSION();
DOS REQUIRED:  1.0 +
SIZE:  5 bytes.
FUNCTION:  calls DOS interrupt to get the version number of the host MS-DOS
	   operating system.
RETURNS:  if DOS version 1
	      AX = 0x3000
	  if DOS version 2.0 +
   	      AL = major version number (example 2.10 would be AL = 2)
	      AH = minor version number (example 4.10 would be AH = 10)


CALLING FORMAT:  GETINTVECT(addressbuf,intnum);
		  addressbuf = address of 2 word buffer for interrupt
			 address.  Low word of interrupt address will
			 be stored at offset 0 and high word at offset
			 2 bytes.
		  intnum = number of the interrupt vector to get.
SIZE:  22 bytes.
FUNCTION:  Copies the address of the interrupt vector into addressbuf.
RETURNS:  AX,BX,CX,DX = undefined
	  ES = 0x0000


CALLING FORMAT:  GETMEM(blocksize);
                  blocksize = size of desired block in 16 byte paragraphs.  
DOS REQUIRED:  2.0 +
SIZE:  10 bytes.
FUNCTION:  Attempts to allcate a memory block of the specified size.
           Returns the address of the allocated memory block.  All
           allocated memory blocks are automatically deallocated when the
           program terminates.
RETURNS:  AX = segment address of allocated memory block, if the value is
               0 then the allocation failed.
          BX = undefined.


CALLING FORMAT:  GETMEMSIZE();
SIZE:  2 bytes.
FUNCTION:  returns the amount of conventional memory available for MS-DOS
	   and application programs, by interrupt 0x12.
RETURNS:  AX = memory size in KiloBytes.


CALLING FORMAT:  GETPIXEL( ,page,x,y);
		  page = graphics page * 256 (usually 0)
		  x = x coordinate of pixel
		  y = y coordinate of pixel
SIZE:  4 bytes.
FUNCTION:  Gets the colour of a pixel on screen when in a graphics mode by
	   BIOS interrupt.
RETURNS:  AH = 0x0D
	  AL = pixel colour


CALLING FORMAT:  GETPIXEL19( ,x, ,y);
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  Gets a pixel from the screen in mode 19 (0x13) graphics mode.
RETURNS:  DX,BX = Undefined.
	  ES = 0xA000 (VGA seg)
	  AL = colour of pixel specified


CALLING FORMAT:  GETRETURNCODE();
DOS REQUIRED:  2.0 +
SIZE:  4 bytes.
FUNCTION:  calls DOS interrupt to get the return code from a child process.
RETURNS: AH = exit type:
		0x00 if normal termination
		0x01 if termination by critical-error handler
		0x02 if termination by int 0x21 function 0x31 or int 0x27
	 AL = return code


CALLING FORMAT:  GETTEXTPOSITION( ,page);
		  page = desired display page * 256
SIZE:  4 bytes.
FUNCTION:  gets the cursor location of a specified screen page by BIOS
	   interrupt.
RETURNS:  AH = 3
	  CH = starting line for cursor
	  CL = ending line for cursor
	  DH = row (y coordinate)
	  DL = column (x coordinate


CALLING FORMAT:  GETVERIFYFLAG();
DOS REQUIRED:  2.0 +
SIZE:  4 bytes.
FUNCTION:  calls DOS interrupt to get the current value of the system verify
	   (read-after-write) flag.
RETURNS: AH = 84
	 AL = 0x00 if verify flag on or
	      0x01 if verify flay off


CALLING FORMAT:  GETVGAPALETTE( ,first,numbertoget,buffer);
		  first = first colour register to get.
		  numbertoget = number of palette values to get.
		  buffer = offset address of buffer.
SIZE:  9 bytes.
FUNCTION:  Calls a BIOS interrupt to get the RGB palette values.  The buffer
	   must be 3 times the number of colour values long in bytes.  This
	   function will only work on VGA or higher graphics cards.
RETURNS:  nothing.


CALLING FORMAT:  GETVIDEOMODE();
DEFINED IN:  VIDEO.H--
SIZE:  4 bytes.
FUNCTION:  Gets the value of the current video mode from a BIOS interrupt.
RETURNS:  AH = # of character column in current mode
	  AL = video mode (see SETVIDEOMODE();)
	  BH = active display page (usually 0)


CALLING FORMAT:  GOTOXY(xloc,yloc);
		  xloc = X coordinate for cursor starting with 0.
		  yloc = Y coordinate for cursor starting with 0.
DEFINED IN:  WRITE.H--
SIZE:  9 bytes.
FUNCTION:  Sets the cursor location on video page 0 to the desired location,
           using a BIOS interrupt.
RETURNS:  AX,BX,DX = undefined.


CALLING FORMAT:  GWRITE(character,attribute);
  		  character = ASCII character code to write.
		  attribute = attribute of text.
DEFINED IN:  GWRITE.H--
SIZE:  6 bytes.
FUNCTION:  Writes a single character to video page 0 in the specifed colour
           using a BIOS interrupt.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  GWRITEDIGITS(wordvalue,attribute);
		  wordvalue = number to be printed.
		  attribute = attribute of text.
DEFINED IN:  GWRITE.H--
SIZE:  69 bytes.
FUNCTION:  Writes the specified number as a sequence of 5 digits to the
           screen on video page 0 of a graphics video mode in the specified
           colour using a BIOS interrupt.
RETURNS:  AX,BX,CX,DX = Undefined.


CALLING FORMAT:  GWRITEINT(intvalue,attribute);
		  intvalue = number to be printed.
		  attribute = attribute of text.
DEFINED IN:  GWRITE.H--
SIZE:  106 bytes.
FUNCTION:  Writes the specified number to the screen on video page 0 of a
           graphics video mode in the specified colour using a BIOS
           interrupt.
RETURNS:  AX,BX,CX,DX = Undefined.


CALLING FORMAT:  GWRITESTRING(stringloc,attribute);
		  stringloc = address of 0 terminating string to be printed.
		  attribute = attribute of text.
DEFINED IN:  GWRITE.H--
SIZE:  17 bytes.
FUNCTION:  Writes the specified string to the screen on video page 0 of a
           graphics video mode in the specified colour using a BIOS
           interrupt.
RETURNS:  AX,BX = Undefined.


CALLING FORMAT:  GWRITEWORD(wordvalue,attribute);
		  wordvalue = number to be printed.
		  attribute = attribute of text.
DEFINED IN:  GWRITE.H--
SIZE:  90 bytes.
FUNCTION:  Writes the specified number to the screen on video page 0 of a
           graphics video mode in the specified colour using a BIOS
           interrupt.
RETURNS:  AX,BX,CX,DX = Undefined.


CALLING FORMAT:  HALT();
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  quits the program by DOS interrupt 0x21 function 0x00.
RETURNS:  never


CALLING FORMAT:  INPORTB( , , ,port);
		  port = port to read byte value from (0 to 65535)
SIZE:  1 byte.
FUNCTION:  reads a byte from a port.
RETURNS:  AL = byte read


CALLING FORMAT:  INPORTW( , , ,port);
		  port = port to read word value from (0 to 65535)
SIZE:  1 byte.
FUNCTION:  reads a word from a port.
RETURNS:  AX = word read


CALLING FORMAT:  KBHIT();
SIZE:  14 bytes.
FUNCTION:  checks to see if a key is waiting to be read from the keyboard
	   buffer.
RETURNS:  AX == 0x0000 if no key is waiting or
	  AX != 0x0000 if at least one key has been pressed


CALLING FORMAT:  KEEP( , , ,offset);
		  offset = offest of the last byte +1 of program to stay
			   resident
DOS REQUIRED:  1.0 +
SIZE:  2 bytes.
FUNCTION:  calls DOS interrupt 0x27 to terminate the program and keep the
	   amount specified of it resident in memory.
RETURNS:  nothing


CALLING FORMAT:  KEYCHECK();
DOS REQUIRED: 1.0 +
SIZE:  4 bytes.
FUNCTION:  calls a dos interrupt to check if a key is waiting to be read from
	   the keyboard.
RETURNS:  AH = undefined
	  AL = 0x00 if no character is available or
    	       0xFF if at least one character is available


CALLING FORMAT:  LOAD8X8FONT();
SIZE:  7 bytes.
FUNCTION:  Loads the 8x8 text font.  This should only be called after a video
	   mode change into a text mode.  On the EGA this function will
	   change the number of text rows from 25 to 43.  On the VGA and
	   higher this function will change the number text rows from 25 to
	   50.  This function will have no effect on video cards below EGA.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  LOAD8X14FONT();
SIZE:  7 bytes.
FUNCTION:  Loads the 8x14 text font.  This should only be called after a
	   video mode change into a text mode.  This function will have no
	   effect on video cards below EGA.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  LOAD8X16FONT();
SIZE:  7 bytes.
FUNCTION:  Loads the 8x16 text font.  This should only be called after a
	   video mode change into a text mode.  This function will have no
	   effect on video cards below the MCGA.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  MAXKEYRATE();
SIZE:  7 bytes.
FUNCTION:  Sets the keyboard repeat rate to maximum.  This function is only
	   available with AT or higher keyboard BIOS.
RETURNS:  AX = undefined
	  BX = 0


CALLING FORMAT:  NOSOUND();
DEFINED IN:  SOUND.H--
SIZE:  6 bytes.
FUNCTION:  Turns off the internal IBM speaker.
RETURNS:  AL = undefined


CALLING FORMAT:  ORPIXEL19( ,x,colour,y);
		  colour = colour of pixel desired ( 0..255)
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  ORs a pixel to the screen in mode 19 (0x13) graphics mode.
RETURNS:  AX,DX,BX = Undefined.
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  OUTPORTB(value, , ,port);
		  value = byte value to write out
		  port = port to write value to (0 to 65535)
SIZE:  1 byte.
FUNCTION:  Writes a byte to a port.
RETURNS:  nothing


CALLING FORMAT:  OUTPORTW(value, , ,port);
		  value = word value to write out
		  port = port to write value to (0 to 65535)
SIZE:  1 byte.
FUNCTION:  Writes a word to a port.
RETURNS:  nothing


CALLING FORMAT:  PASSTR( , , , ,cstringoffset,passtringoffset);
		  cstringoffset = offset address of C type string.
		  passtringoffset = offset address of Pascal type string.
SIZE:  23 bytes.
FUNCTION:  Copies a Pascal type string to a C type string.  A Pascal type 
           string is a string whos first byte specifies the length of the
           string.  A C type string is a string which is terminated with
           the byte value zero.
RETURN:  AX = length of the new string, not including the 0 terminator
         CX = 0
         ES = DS
         DI,SI = undefined


CALLING FORMAT:  PUTBRICK19( , ,xlen,ylen,screenloc,bufloc);
		  xlen = the width of the block in bytes
		  ylen = the length of the block in pixels
		  screenloc = start memory location offset to write to
		  bufloc = location of the buffer
SIZE:  bytes.
FUNCTION:  Puts the image of bytes from the buffer on to the current VGA
	   graphics screen from at the location specified.
RETURNS:  ES = DS
	  SI = end of buffer
	  AX,DI = undefined
	  CX,DX = 0
	  BX = xlen


CALLING FORMAT:  PUTPIXEL(colour,page,x,y);
		  colour = colour of pixel desired
		  page = graphics page * 256 (usually 0)
		  x = x coordinate of pixel
		  y = y coordinate of pixel
SIZE:  4 bytes.
FUNCTION:  Writes a pixel to the screen when in a graphics mode.
RETURNS:  AH = 0x0C


CALLING FORMAT:  PUTPIXEL19( ,x,colour,y);
		  colour = colour of pixel desired ( 0..255)
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  Puts a pixel to the screen in mode 19 (0x13) graphics mode.
RETURNS:  AX,DX,BX = Undefined.
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  REBOOT();
SIZE:  2 bytes.
FUNCTION:  Calls reboot interrupt 0x19 (just an INT 0x19 instruction).
RETURNS:  should not return.


CALLING FORMAT:  READSTRING( , , ,string);
		  string = location of string to be read into,
			   first byte contains maximum length,
			   second byte will contain number of characters
                           read, remaining bytes will contain the string
                           read including the ending carrage return.
DOS REQUIRED:  1.0 +
SIZE:  4 bytes.
FUNCTION:  reads a string from the keyboard by DOS interrupt.
RETURNS:  AH = 10


CALLING FORMAT:  SETATIMASK( ,readwritemask);
		  readwritemask = memory page to select.
SIZE:  36 bytes.
FUNCTION:  Sets the current video memory page for memory read/write
           operations for the ATI VGA Wonder card for its enhanced graphics
           modes.  This function is only available on ATI VGA Wonder or
           higher ATI graphics cards.
RETURNS:  AX,BX,DX = undefined


CALLING FORMAT:  SETBORDERCOLOR(color);
		  color = color desired for border.
SIZE:  7 bytes.
FUNCTION:  Sets the border to the color specified.  This function is only 
           available with PCjr, EGA, VGA or higher graphics cards.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  SETCURRENTDIR(stringpath);
		  stringpath = offset address of pathname string.
DOS REQUIRED:  2.0 +
SIZE:  10 bytes.
FUNCTION:  Sets the current directory for the drive specified in the path 
           string to the directory in the path string.
RETURNS:  AX == 0 if successful
          AX != 0 if unsuccessful
          DX = stringpath


CALLING FORMAT:  SETCURRENTDRIVE(drivecode);
		  drivecode = drive number, 0 = A, 1 = B, etc.
DOS REQUIRED:  1.0 +
SIZE:  12 bytes.
FUNCTION:  Sets the current drive to the value specified in drivecode.
RETURNS:  AX == 0 if successful
          AX != 0 if unsuccessful
          DL = drivecode


CALLING FORMAT:  SETDISPLAYPAGE(page);
SIZE:  4 bytes.
FUNCTION:  Sets the current display page for the current video mode.  
           Total number of video pages for each video mode depends on the
           installed graphics card.  Below is a list of available video pages
           for each video mode and video card:
             mode: 0x0,0x1     - 0 to 7 for CGA, EGA, MCGA, VGA, and XGA
                   0x2,0x3     - 0 to 3 for CGA
                               - 0 to 7 for EGA, MCGA, VGA, and XGA
                   0x7         - 0 to 7 for EGA, VGA, and XGA
                   0xD         - 0 to 7 for EGA, VGA, and XGA
                   0xE         - 0 to 3 for EGA, VGA, and XGA
                   0xF         - 0 to 1 for EGA, VGA, and XGA
                   0x10        - 0 to 1 for EGA, VGA, and XGA
RETURNS:  AX = undefined


CALLING FORMAT:  SETINTVECT( ,intnum,segmentvalue,offsetvalue);
		  intnum = number of the interrupt vector to get.
		  segmentvalue = segment value for the new interrupt
		  	         vector.
		  offsetvalue = offset value for the new interrupt
			        vector.
SIZE:  17 bytes.
FUNCTION:  Sets the specified interrupt vector with the address given.
RETURNS:  AX,BX = undefined
	  CX = segmentvalue
	  DX = offsetvalue
	  ES = 0x0000


CALLING FORMAT:  SETSCREENOFFSET( ,offset);
		  offset = value to set offset of the screen
SIZE:  20 bytes.
FUNCTION:  Sets the offset address of the video RAM for display.  This
	   function will only work on CGA and higher colour graphics
	   cards.
RETURNS:  AL,DX = undefined


CALLING FORMAT:  SETSCREENOFFSETM( ,offset);
		  offset = value to set offset of the screen
SIZE:  20 bytes.
FUNCTION:  Sets the offset address of the video RAM for display.  This
	   function will only work on monocrome graphics cards.
RETURNS:  AL,DX = undefined


CALLING FORMAT:  SETTEXTPOSITION( ,page, ,loc);
		  page = desired display page * 256
		  loc = row * 256 + column
SIZE:  4 bytes.
FUNCTION:  Sets the cursor to a location specified on the screen.
RETURNS:  AH = 2


CALLING FORMAT:  SETTICKINTERVAL( ,intervalsize);
		  intervalsize = value sent to timer 0 (see below).
SIZE:  14 bytes.
FUNCTION:  Sets the interval time between pulses from PIT, which causes
	   calls to INT 8h.  The initial value of the interval is 0xFFFF
	   for 18.200 times a second.  A value of 0x7FFF is about 36.4
	   times a second.  Changing this value has many side effects,
	   speeding up of the system clock (but not the CMOS clock), faster
	   shut off time of floppy drive motors and mutation of speed ratings
	   from CPU testing programs.  Many things depend on the clock
	   interrupt and I remove myself from any fault for system damage
	   by changing this value, even though I feel that the worst that
	   can happen is a system crash, but hard drives seem to crash when
	   they want to...
RETURNS:  AL = undefined.


CALLING FORMAT:  SETVGADAC(first, ,numbertoset, , ,buf);
		  first = first palette value to set (0 to 255).
		  numbertoset = number of palette values to set times 3.
		  buf = offset address of buffer to read from.
SIZE:  9 bytes.
FUNCTION:  Set the DAC register values on the VGA card, resulting in palette
	   selection.  This will only work on a 80286 or higher processor
	   with VGA or higher graphics card.
RETURNS:  AX,DX,SI = undefined.
NOTE:  This procedure executes 286 operations, 80286 or greater processor
       required to execute.


CALLING FORMAT:  SETVGAPALETTE( ,first,numbertoset,buffer);
		  first = first colour register to set.
		  numbertoset = number of palette values to set.
		  buffer = offset address of buffer.
SIZE:  9 bytes.
FUNCTION:  Calls a BIOS interrupt to set the RGB palette values.  The buffer
	   must be 3 times the number of colour values long in bytes.  This
	   function will only work on VGA or higher graphics cards.
RETURNS:  nothing.


CALLING FORMAT:  SETVIDEOMODE(mode);
	  mode = graphics mode value (see below):
		   mode  X by Y  colours  type      graphics-card-required
		 0   40x25      16    text       CGA,PCjr,EGA,MCGA,VGA
		 1   40x25      16    text       CGA,PCjr,EGA,MCGA,VGA
		 2   80x25      16    text       CGA,PCjr,EGA,MCGA,VGA
		 3   80x25      16    text       CGA,PCjr,EGA,MCGA,VGA
		 4   320x200     4  graphics     CGA,PCjr,EGA,MCGA,VGA
		 5   320x200     4  graphics     CGA,PCjr,EGA,MCGA,VGA
		 6   640x200     2  graphics     CGA,PCjr,EGA,MCGA,VGA
		 7   80x25       2    text   MDA,         EGA,     VGA
		 8   160x200    16  graphics         PCjr,
		 9   320x200    16  graphics         PCjr,
		10   640x200     4  graphics         PCjr,
		13   320x200    16  graphics              EGA,     VGA
		14   640x200    16  graphics              EGA,     VGA
		15   640x350     2  graphics              EGA,     VGA
		16   640x350    16  graphics              EGA,     VGA
		17   640x480     2  graphics                  MCGA,VGA
		18   640x480    16  graphics                       VGA
		19   320x200   256  graphics                  MCGA,VGA
		20   640x400    16  graphics Tecmar VGA/AD ONLY
		22   800x600    16  graphics Tecmar VGA/AD ONLY
		23   132x25     16    text   Tecmar VGA/AD ONLY
		24   1024x768   16  graphics Tecmar VGA/AD ONLY
		24   132x44      2    text   Tseng Labs EVA ONLY
		25   132x25      2    text   Tseng Labs EVA ONLY
		26   132x28      2    text   Tseng Labs EVA ONLY
		26   640x350   256  graphics Tecmar VGA/AD ONLY
		27   640x400   256  graphics Tecmar VGA/AD ONLY
		28   640x480   256  graphics Tecmar VGA/AD ONLY
		29   800x600   256  graphics Tecmar VGA/AD ONLY
		34   132x44     16    text   Tseng Labs EVA ONLY
		34   132x44     16    text   Ahead Systems EGA2001 ONLY
		34   132x43     16    text   Allstar Peacock VGA ONLY
		35   132x25     16    text   ATI EGA, ATI VGA ONLY
		35   132x25     16    text   Tseng Labs EVA ONLY
		35   132x25     16    text   Ahead Systems EGA2001 ONLY
		35   132x28     16    text   Allstar Peacock VGA ONLY
		36   132x28     16    text   Tseng Labs EVA ONLY
		36   132x25     16    text   Allstar Peacock VGA ONLY
		37   640x480    16  graphics VEGA VGA ONLY
		38   640x480    16  graphics Ahead Systems EGA2001 ONLY
		39   132x25      2    text   ATI EGA, ATI VGA ONLY
		39   720x512    16  graphics Genoa or VEGA VGA ONLY
		41   800x600    16  graphics Orchid,STB,Genoa,Sigma,VEGA ONLY
		41   800x600    16  graphics Allstar Peacock VGA ONLY
		42   100x40     16    text   Allstar Peacock VGA ONLY
		42   100x40     16    text   Orchid Prodesigner VGA ONLY
		45   640x350   256  graphics Genoa,STB,VEGA VGA ONLY
		46   640x480   256  graphics Orchid,STB,Genoa,Sigma,VEGA ONLY
		47   720x512   256  graphics Genoa or VEGA VGA ONLY
		48   800x600   256  graphics Orchid,STB,Genoa,Sigma,VEGA ONLY
		51   132x44     16    text   ATI EGA or ATI VGA ONLY
		54   960x720    16  graphics STB or VEGA VGA
		55   132x44      2    text   ATI EGA or ATI VGA ONLY
		55   1024x768   16  graphics Orchid,STB,Genoa,Sigma,VEGA ONLY
		65   132x25     16    text   Tatung, Video7, VEGA VGA ONLY
		66   132x43     16    text   Tatung, Video7, VEGA VGA ONLY
		67   80x60      16    text   Tatung, Video7, VEGA VGA ONLY
		68   100x60     16    text   Tatung, Video7, VEGA VGA ONLY
		69   132x28     16    text   Tatung, Video7, VEGA VGA ONLY
		77   120x25     16    text   VEGA VGA ONLY
		78   120x43     16    text   VEGA VGA ONLY
		79   132x25     16    text   VEGA VGA ONLY
		80   80x43       2    text   VEGA VGA ONLY
		80   132x25      2    text   Ahead Systems EGA2001 ONLY
		81   80x34      16    text   ATI EGA ONLY
		81   132x25      2    text   VEGA VGA ONLY
		82   132x44      2    text   Ahead Systems EGA2001 ONLY
		82   132x43      2    text   VEGA VGA ONLY
		82   94x29      16    text   ATI EGA Wonder ONLY
		83   800x600    16  graphics ATI EGA or ATI VGA ONLY
		84   800x600    16  graphics ATI EGA, ATI VGA ONLY
		84   132x43     16    text   Paradise VGA,Taxan 565 EGA ONLY
		84   132x43     16    text   AST VGA Plus ONLY
		84   132x43     16    text   Hewlett-Packard D1180A ONLY
		85   132x25     16    text   Paradise VGA,Taxan 565 EGA ONLY
		85   132x25     16    text   AST VGA Plus ONLY
		85   132x25     16    text   Hewlett-Packard D1180A ONLY
		86   800x600    16  graphics ATI EGA or ATI VGA ONLY
		86   800x600    16  graphics Paradise or AT&T VDC600 ONLY
		86   800x600    16  graphics AST VGA Plus or Compaq VGA ONLY
		86   800x600    16  graphics Dell VGA ONLY
		86   800x600    16  graphics Hewlett-Packard D1180A ONLY
		89   800x600     2  graphics Paradise, AT&T VDC600 ONLY
		89   800x600     2  graphics ATI VIP, AST VGA Plus ONLY
		89   800x600     2  graphics Compaq VGA, Dell VGA ONLY
		89   800x600     2  graphics Hewlett-Packard D1180A ONLY
		94   640x400   256  graphics Paradise VGA or VEGA VGA ONLY
		94   640x400   256  graphics AST VGA Plus, Compaq VGA ONLY
		94   640x400   256  graphics Dell VGA or AT&T VDC600 ONLY
		95   640x480   256  graphics AST VGA Plus, Compaq VGA ONLY
		95   640x480   256  graphics Dell VGA or AT&T VDC600 ONLY
		95   640x480   256  graphics Paradise VGA ONLY
		96   752x410    16  graphics VEGA VGA,Tatung VGA,Video7 ONLY
		97   720x540    16  graphics VEGA VGA,Tatung VGA,Video7 ONLY
		97   640x400   256  graphics ATI VGA ONLY
		98   640x480   256  graphics ATI VGA ONLY
		98   800x600    16  graphics VEGA VGA,Tatung VGA,Video7 ONLY
		99   800x600   256  graphics ATI VGA ONLY
		99   1024x768    2  graphics Video7 V-RAM VGA ONLY
	       100   1024x768    4  graphics Video7 V-RAM VGA ONLY
	       101   1024x768   16  graphics ATI VGA, Video7 V-RAM VGA ONLY
	       102   640x400   256  graphics Tatung VGA, Video7 V-RAM ONLY
	       103   640x480   256  graphics Video7 V-RAM VGA ONLY
	       103   1024x768    4  graphics ATI VGA Wonder ONLY
	       105   720x540   256  graphics Video7 V-RAM VGA ONLY
	       106   800x600    16  graphics VESA standard interface ONLY
	       124   512x512    16  graphics Genoa ONLY
	       125   512x512   256  graphics Genoa ONLY
DEFINED IN:  VIDEO.H--
SIZE:  4 bytes.
FUNCTION:  Sets the current video mode by BIOS interrupt.
RETURNS:  nothing


CALLING FORMAT:  SHIFTSTATUS();
SIZE:  9 bytes.
FUNCTION:  returns the current state of the shift, ctrl, alt, and other keys.
RETURNS:  AX = bit 0 =1 if right shift key is depressed
    	       bit 1 =1 if left shift key is depressed
	       bit 2 =1 if control key is depressed
	       bit 3 =1 if alt key is depressed
	       bit 4 =1 if scroll lock state is on
	       bit 5 =1 if number lock state is on
	       bit 6 =1 if caps lock state is on
	       bit 7 =1 if insert state is on
	       bit 8 = undefined
	       bit 9 = undefined
	       bit 10 = undefined
	       bit 11 =1 if control number lock state is on
	       bit 12 =1 if scroll lock key is depressed
	       bit 13 =1 if number lock key is depressed
	       bit 14 =1 if caps lock key is depressed
	       bit 15 =1 if insert key is depressed
	  ES = 0x0000


CALLING FORMAT:  SOUND(frequency);
		  frequency = frequency of sound desired in Hz.
DEFINED IN:  SOUND.H--
SIZE:  30 bytes.
FUNCTION:  Starts the internal IBM speaker (wow) to emit a sound at the
           desired frequency (aprox. range 50 to 12000 Hz).
RETURNS:  AX,BX,DX = undefined


CALLING FORMAT:  STRCAT( , , , ,deststrffset,sourcestroffset);
		  deststroffset = offset address of destination string.
		  sourcestroffset = offset address of source string.
SIZE:  23 bytes.
FUNCTION:  Copies the source string on to the end of the destination 
           string.
RETURNS:  AX,BX,CX,DI,SI = undefined.


CALLING FORMAT:  STRLEN(stroffset);
		  stroffset = memory location of string
SIZE:  13 bytes.
FUNCTION:  Calculates the length of the string which is terminated by the
           byte value of zero.
RETURNS:  AX and BX = length of string in bytes excluding terminating byte.
         

CALLING FORMAT:  STRPAS( , , , ,passtringoffset,cstringoffset);
		  passtringoffset = offset address of Pascal type string.
		  cstringoffset = offset address of C type string.
SIZE:  24 bytes.
FUNCTION:  Copies a C type string to a Pascal type string.  A Pascal type 
           string is a string whos first byte specifies the length of the
           string.  A C type string is a string which is terminated with
           the byte value zero.
RETURNS:  AX,BX,CX,DI,SI = undefined.


CALLING FORMAT:  SUBPIXEL19( ,x,colour,y);
		  colour = colour of pixel desired ( 0..255)
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  subtracts a pixel from the screen in mode 19 (0x13) graphics mode.
RETURNS:  AX,DX,BX = undefined
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  TEXTROWS();
SIZE:  8 bytes.
FUNCTION:  Returns the number of text rows on screen minus one.
RETURNS:  AL = number of text rows - 1
	  ES = 0x0000


CALLING FORMAT:  TURNOFFCHAIN4();
SIZE:  53 bytes.
FUNCTION:  Disactivates the chain 4 memory organization for video mode
           320x200 256 colours.  Thus allowing all 4 memory planes to be
           addressed.
RETURNS:  DX,AX = undefined


CALLING FORMAT:  UNBLANKVGA();
SIZE:  6 bytes.
FUNCTION:  Restores the screen after a call to BLANKVGA().  This is done by
	   by resetting the DAC mask register back to 0xFF.
RETURNS:  AL = 0xFF
	  DX = 0x3C6


CALLING FORMAT:  WARMBOOT();
SIZE:  15 bytes.
FUNCTION:  Warm boots the computer.
RETURNS:  Never Ever


CALLING FORMAT:  WAITVSYNC();
SIZE:  13 bytes.
FUNCTION:  Waits for the leading edge of vertical sync pulse, marking the
	   beginning of the vertical non-display period.
RETURNS:  AX,DX undefined.


CALLING FORMAT:  WINDOWDOWN(numoflines,attribute,upperleftloc,lowerrightloc);
		  numoflines = number of lines to scroll, 1 to 255
		  attribute = attribute to be used for blanked area
		  upperleftloc = CH =Y coordinate + CL =X coordinate of the
				 upper left corner of the window
	 	  lowerrightloc = DH =Y coordinate + DL =X coordinate of the
				  upper left corner of the window
DEFINED IN:  WRITE.H--
SIZE:  7 bytes.
FUNCTION:  scrolls a specified window down a number of lines and initializes
	   the new lines with the attribute given.
RETURNS:  AH = 0x06
	  BH = attribute


CALLING FORMAT:  WINDOWUP(numoflines,attribute,upperleftloc,lowerrightloc);
		  numoflines = number of lines to scroll, 1 to 255
		  attribute = attribute to be used for blanked area
		  upperleftloc = CH =Y coordinate + CL =X coordinate of the
				 upper left corner of the window
		  lowerrightloc = DH =Y coordinate + DL =X coordinate of the
				  upper left corner of the window
DEFINED IN:  WRITE.H--
SIZE:  7 bytes.
FUNCTION:  scrolls a specified window up a number of lines and initializes
	   the new lines with the attribute given.
RETURNS:  AH = 0x06
	  BH = attribute


CALLING FORMAT:  WORDTODIGITS(number,stringloc);
		  number = word to be converted to digits string
		  stringloc = location of string
SIZE:  59 bytes.
FUNCTION:  converts a word value to 5 decimal digits and a NULL terminating
	   character.
RETURNS:  CX,DX = undefined
	  AX = AX % 10


CALLING FORMAT:  WRITE(character);
 		  character = ASCII character code to write.
DEFINED IN:  WRITE.H--
SIZE:  7 bytes.
FUNCTION:  Writes a single character to video page 0 using a BIOS
	   interrupt.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  WRITEDIGITS(wordvalue);
		  wordvalue = number to be printed.
DEFINED IN:  WRITE.H--
SIZE:  70 bytes.
FUNCTION:  Writes the specified number as a sequence of 5 digits to video
           page 0 using a BIOS interrupt.
RETURNS:  AX,BX,CX,DX = Undefined.


CALLING FORMAT:  WRITEINT(intvalue);
		  intvalue = number to be printed.
DEFINED IN:  WRITE.H--
SIZE:  107 bytes.
FUNCTION:  Writes the specified number to video page 0 using a BIOS
           interrupt.
RETURNS:  AX,BX,CX,DX = Undefined.


CALLING FORMAT:  WRITELN();
DEFINED IN:  WRITE.H--
SIZE:  12 bytes.
FUNCTION:  Writes a carrage return and linefeed to video page 0 using a BIOS
           interrupt.  This results in the cursor being moved to the
           beginning of the next line.
RETURNS:  AX,BX = undefined


CALLING FORMAT:  WRITESTR(stringloc);
		  stringloc = address of 0 terminating string to be printed.
DEFINED IN:  WRITE.H--
SIZE:  18 bytes.
FUNCTION:  Writes the specified string to video page 0 using a BIOS
           interrupt.
RETURNS:  AX,BX = Undefined.


CALLING FORMAT:  WRITEWORD(wordvalue);
		  wordvalue = number to be printed.
DEFINED IN:  WRITE.H--
SIZE:  91 bytes.
FUNCTION:  Writes the specified number to video page 0 using a BIOS
           interrupt.
RETURNS:  AX,BX,CX,DX = Undefined.


CALLING FORMAT:  XLINE19(x,y,length,colour);
		  x = x coordinate of start of line (0..319)
		  y = y coordinate of start of line (0..199)
                  length = pixel lenght of line (1..200)
		  colour = colour of pixel desired (0..255)
SIZE:  20 bytes.
FUNCTION:  Draws a horizontal line to the screen in mode 19 (0x13) graphics
           mode of the specified length and colour.
RETURNS:  AX,BX,DX,DI = Undefined.
          CX = 0
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  XORPIXEL19( ,x,colour,y);
		  colour = colour of pixel desired (0..255)
		  x = x coordinate of pixel (0..319)
		  y = y coordinate of pixel (0..199)
SIZE:  15 bytes.
FUNCTION:  XORs a pixel to the screen in mode 19 (0x13) graphics mode.
RETURNS:  AX,DX,BX = Undefined.
	  ES = 0xA000 (VGA seg)


CALLING FORMAT:  YLINE19(x,y,length,colour);
		  x = x coordinate of start of line (0..319)
		  y = y coordinate of start of line (0..199)
                  length = pixel lenght of line (1..320)
		  colour = colour of pixel desired (0..255)
SIZE:  25 bytes.
FUNCTION:  Draws a vertical line to the screen in mode 19 (0x13) graphics
           mode of the specified length and colour.
RETURNS:  AX,BX,DX,DI = Undefined.
          CX = 0
	  ES = 0xA000 (VGA seg)


/* end of REGPROCS.DOC */