===========================================================
                DDDDD           DDDDD               SSSS
                 D   Dunfield    D   D             S
                 D   D           D   Development    SSSS 
                 D   D           D   D                  Systems
                DDDDD           DDDDD               SSSS
          ===========================================================
          MM   MM  IIIIIII    CCCC   RRRRRR     OOO             CCCC
          M M M M     I      C    C  R     R   O   O           C    C
          M  M  M     I     C        R     R  O     O         C
          M     M     I     C        RRRRRR   O     O  -----  C
          M     M     I     C        R   R    O     O         C
          M     M     I      C    C  R    R    O   O           C    C
          M     M  IIIIIII    CCCC   R     R    OOO             CCCC
          ===========================================================
    
    
    
    
    
                             A compact 'C' compiler
                                      for
                                 Small Systems.
    
    
                                Technical Manual
    
    
    
    
    
                                  Release 3.1
    
                               Revised 14-Apr-94
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1988-1994 Dave Dunfield
                              All rights reserved

    MICRO-C                                                          Page: 1


    1. INTRODUCTION
    
          DDS MICRO-C is a compact, portable compiler for the  'C'  language
       which is suitable for implementation on small 8 or  16  bit  computer
       systems. It may be used as a  resident  or  cross  compiler,  and  is
       capable of generating ROMable code. It is distributed in source form,
       and thus provides a learning tool for those wishing  to  examine  the
       internals of a working compiler.
    
          The main goal in the development of MICRO-C, has been to provide a
       reasonably powerful language  which  will  be  portable  with  little
       difficulty to many  target  systems.  The  'C'  language  was  chosen
       because  it  was  designed  to  be  portable,  and   provides   ample
       programming power. MICRO-C provides  an  alternative  to  interpreted
       BASIC or assembly language  programming  which  are  often  the  only
       languages available on small 8 bit systems.
    
          With today's focus on larger computers and workstations,  software
       support for small  systems  and  micro-controller  sized  devices  is
       getting both hard to find, and expensive.  MICRO-C  helps  fill  that
       gap, because all files necessary to port and  maintain  the  compiler
       are included on the distribution disks, allowing it to  be  moved  to
       ANY system without dependance on a software vendor.
    
          Included in this package is a complete  IBM/PC  implementation  of
       MICRO-C, with a comprehensive  library,  which  you  may  use  as  an
       example installation. This implementation of  the  compiler  requires
       the Microsoft MASM (or compatible) assembler.
    
          The MICRO-C "package" (software and documentation) is copyrighted,
       and may  not  be  re-distributed  in  any  form  without  my  written
       permission. If you have received the  "DEMO"  archive,  and  wish  to
       obtain the entire MICRO-C package complete with source code, fill out
       and send the order form contained in the "READ.ME" file,  along  with
       the required payment to:
    
                           Dunfield Development Systems
                           P.O. Box 31044
                           Nepean, Ontario (Canada)
                           K2B 8S8
    
          Please make your  cheque  or  money  order  payable  to  "Dunfield
       Development Systems".
    
          MICRO-C is provided on an "as is" basis, with no warranty  of  any
       kind. In no event shall the author be liable for any damages  arising
       from its use or distribution.

    MICRO-C                                                          Page: 2


       1.1 Compiler Portability
    
             MICRO-C is written in standard 'C', and is capable of compiling
          itself. This allows any system  with  a  'C'  compiler  (including
          MICRO-C) to be used to port MICRO-C to another processor.
    
             The  parser  makes  very  few  assumptions  about  the   target
          processor  or  operating  system  architecture,  allowing  a  code
          generator  to  be  written  for  virtually   any   processor   and
          environment.
    
             With the exception of required I/O routines (described  later),
          the MICRO-C compiler uses no library functions, and relies  on  no
          system services.
    
             Assuming that the code generator is fairly efficent,  and  that
          the I/O routines and code generator are not unreasonably large,  a
          full MICRO-C compiler may be implemented on systems with as little
          as 32K of free ram and a single floppy disk.
    
       1.2 Code Portability
    
             With few exceptions, this compiler follows the  syntax  of  the
          "standard" UNIX compiler (within  its  subset  of  the  language).
          Programs written in MICRO-C should compile with few changes  under
          other "standard" compilers.
    
          1.2.1 Unsupported Features:
    
                MICRO-C does not currently support the following features of
             standard 'C':
    
                    Long / Double / Float / Enumerated data types,
                    Typedef and Bit fields.
    
          1.2.2 Additional Features
    
                MICRO-C provides a few additional  features  which  are  not
             always included in "standard" 'C' compilers:
    
                    Unsigned character variables, Nested comments, 16 bit
                    character constants, Inline assembly code capability.

    MICRO-C                                                          Page: 3


       1.3 The compiling process
    
             There are five  programs  which  work  together  to  completely
          compile a MICRO-C program:
    
             The PREPROCESSOR (MCP) takes  the  original  'C'  source  file,
          performs MACRO expansion and incorporates the contents of  INCLUDE
          files  to  get  a  "pure"  'C'  output  file.  A   less   powerful
          pre-processor is also contained inside the COMPILER, which  allows
          this step to  be  skipped  for  programs  which  use  only  simple
          pre-processor functions.
    
             The COMPILER  (MCC)  reads  a  file  containing  a  'C'  source
          program, and translates it into an  equivalent  assembly  language
          program.
    
             The OPTIMIZER (MCO) reads the assembly language output from the
          compiler identifying and replacing "general" code produced by  the
          compiler with more efficent code which is equivalent  in  specific
          cases. This step is  optional,  allowing  you  to  choose  between
          faster compile time and greater program efficency.
    
             The ASSEMBLER takes  the  assembly  language  produced  by  the
          COMPILER or OPTIMIZER, and produces an OBJECT FILE which  contains
          the executable code and external reference map for the program.
    
             The LINKER combines the executable code from  the  OBJECT  FILE
          with code from  other  programs  which  it  calls  (including  any
          LIBRARY functions), to produce a complete  stand-alone  executable
          program.
    
             The ASSEMBLER and LINKER  are  NOT  included  as  part  of  the
          MICRO-C package. These programs are  specific  to  the  particular
          system, and must be obtained from the system vendor.
    
             Some cross ASSEMBLER's do  not  produce  an  object  file,  but
          generate the executable program directly  instead.  These  systems
          assume that the ENTIRE program is completely contained in a SINGLE
          assembly language file. This type  of  system  prevents  you  from
          using a object LIBRARY which is  an  integral  feature  of  any  C
          programming system.
    
             To  accomodate  this  type  of  development   system,   without
          sacrificing the ability to use a LIBRARY,  a  program  called  the
          SOURCE LINKER (SLINK)  is  included  with  MICRO-C.  This  program
          combines your program  with  library  functions  at  the  ASSEMBLY
          LANGUAGE level, allowing the entire program code to  be  presented
          to the assembler in a single file. See the section  entitled  "THE
          SOURCE LINKER" for additional information.

    MICRO-C                                                          Page: 4


    2. THE COMMAND CO-ORDINATOR
    
          'CC' is a utility which co-ordinates  the  execution  of  programs
       required for each step of the compilation process to provide a simple
       "one step" compilation  command.  This  MICRO-C  package  includes  a
       version of  the  command  co-ordinator  which  handles  the  commands
       necessary to compile for the 8086 processor  (MCP,  MCC,  MCO,  MASM,
       LINK and EXE2BIN). This program  can  be  modified  as  necessary  to
       handle other processors.
    
       2.1 The CC command
    
             The format of the 'CC' command is:
    
                              CC <name> [options]
    
          2.1.1 Command line options
    
                -A      - produce ASSEMBLER (.ASM) output file
                -C      - Include 'C' source as comments in ASM files
                -F      - Fold identical string constants.
                -K      - KEEP all temporary files (do not delete)
                -L      - produce LINKABLE  (.OBJ) output file
                -O      - OPTIMIZE the output code (using MCO)
                -P      - use the extended PRE-PROCESSOR (MCP)
                -Q      - QUIET mode (suppress informational messages)
                -S      - produce SMALL-MODEL (.EXE) output file
                H=mcdir - specify MICRO-C home directory
                T=mctmp - specify prefix for TEMPORARY files
    
                name=xx - Predefine macro symbol (use with -P only)
    
                When executing the sub-commands, CC will search the  MICRO-C
             home directory, as well as any  directories  specified  in  the
             'PATH' environment variable. Libraries are  accessed  from  the
             MICRO-C home directory only.
    
                The environment variable 'MCDIR' is  examined  to  determine
             the path to  the  MICRO-C  home  directory.  If  MCDIR  is  not
             defined, CC will assume the string '\MC'. You may override this
             directory by using the 'h=' option on the command line.
    
                Intermediate  results  from  each  command  are  stored   in
             "temporary" files, which are fed as input to the next  command.
             Temporary files will be deleted once they are no longer needed,
             except in the case where a command fails.  When  this  happens,
             any temporary file which  was  being  used  as  input  to  that
             command will not be deleted, allowing you to examine it for the
             cause of the error.

    MICRO-C                                                          Page: 5


                The environment variable 'MCTMP' is examined to determine  a
             prefix to prepend to temporary file  names.  If  MCTMP  is  not
             defined, CC assumes the default prefix of '$'. You may override
             this prefix by using the 't=' option on the command line.
    
                Here are example 'SET' commands suitable  for  inclusion  in
             the AUTOEXEC.BAT file, of an IBM/PC based MICRO-C system  which
             has the home directory in 'C:\MC', and a TEMP  directory  on  a
             RAMDISK as drive 'D':
    
                    SET MCDIR=C:\MC
                    SET MCTMP=D:\TEMP\      (Note trailing '\')
    
                The '-A' option  causes  CC  to  bypass  the  assembler  and
             linker, and produce an assembly source file (<name>.ASM) as the
             output file. If the '-C' option is also used,  this  file  will
             contain the 'C' source code in the form of comments. NOTE:  The
             source code inserted by '-C' will  restrict  the  optimizer  to
             operate only on sections of code produced by a single 'C' line.
    
                The '-F' option causes the compiler to  "fold"  its  literal
             pool (the area of memory where string  constants  are  stored).
             This means that identical strings  not  contained  in  explicit
             variables, will occur only once in memory. Since most  programs
             never modify such strings, it is usually safe to do this.  Note
             however that this is a violation of the 'C' standard ("The  'C'
             Programming Language"  page  181  -  "All  strings,  even  when
             written identically, are distinct"),  and  it  is  possible  to
             write programs which will not work properly when this option is
             used.
    
                The '-L' option causes CC to  bypass  the  link  stage,  and
             produce a linkable object module  (<name>.OBJ)  as  the  output
             file.
    
                The '-S' option causes CC to  link  the  program  using  the
             SMALL  memory  model,   and   produce   an   executable   image
             (<name>.EXE) as the output file. This option  applies  only  to
             those  processors  which  have  a  segmented  architecture  and
             multiple memory models such as the 8086.
    
                If none of '-A', '-L' or '-S' is specified, CC will link the
             program using the TINY memory  model,  and  produce  a  command
             image (<name>.COM) as the output file.
    
                If any of the programs  executed  by  CC  fail  to  complete
             properly, CC will show the message "PGM failed (RC)", where PGM
             is the name of the offending program, and RC is the DOS  return
             code value. Common RC values under MSDOS are:
    
                2   - Command not found (Check MCDIR and PATH setup)
                3   - Path not found    (Check MCDIR and PATH setup)
                254 - Program found errors during processing
                255 - Program was invoked with incorrect arguments

    MICRO-C                                                          Page: 6


       2.2 Using multiple object modules
    
             The 'LC' command takes one or more object modules  produced  by
          'CC' with the '-L' option, and links them with  the  libraries  to
          produce an executable module. This module will be given  the  name
          of the first file specified in the argument list.
    
             When compiling large programs which have more than  one  source
          file, you must first compile all modules using 'CC' with the  '-L'
          option, and the use 'LC' to link the resultant object  files  into
          the final executable program.
    
             The '-S' option may be used as the FIRST argument, to cause  LC
          to link in the SMALL model.
                eg: CC FIRST -L
                    CC SECOND -L
                    LC FIRST SECOND         <-- TINY  Model
                    LC -S FIRST SECOND      <-- SMALL Model
    
             The exact syntax  and  options  available  for  'CC'  and  'LC'
          commands may differ in specific implementations of  the  compiler.
          See the 'READ.ME' file and any additional technical  documentation
          on your distribution disk(s) for details.

    MICRO-C                                                          Page: 7


    3. THE MICRO-C PROGRAMMING LANGUAGE
    
          The following pages contain a brief summary of  the  features  and
       constructs implemented in MICRO-C.
    
          This document does not  attempt  to  teach  'C'  programming,  and
       assumes that the reader is familiar with the language.
    
       3.1 Constants
    
             The following forms of constants are supported by the compiler:
    
                <num>       - Decimal number        (0 - 65535)
                0<num>      - Octal number          (0 - 0177777)
                0x<num>     - Hexidecimal number    (0x0 - 0xffff)
                '<char>'    - Character             (1 or 2 chars)
                "<string>"  - Address of literal string.
    
             The following "special" characters may be used within character
          constants or strings:
    
                \n          - Newline (line-feed)   (0x0a)
                \r          - Carriage Return       (0x0d)
                \t          - Tab                   (0x09)
                \f          - Formfeed              (0x0c)
                \b          - Backspace             (0x08)
                \<num>      - Octal value <num>     (Max. three digits)
                \x<num>     - Hex value <num>       (Max. two digits)
                \<char>     - Protect character <char> from input scanner.
    
       3.2 Symbols
    
             Symbol names  may  include  the  characters  'a'-'z',  'A'-'Z',
          '0'-'9', and '_'. The characters '0'-'9' may not be  used  as  the
          first character in the  symbol  name.  Symbol  names  may  be  any
          length, however, only the first 15 characters are significant.
    
             The "char" modifier may be used to declare a symbol as an 8 bit
          wide value, otherwise it is assumed to be 16 bits.
    
                              eg: char input_char;
    
             The "int" modifier may be used to declare a symbol as a 16  bit
          wide value. This is assumed if neither "int" or "char" is given.
    
                                  eg: int abc;
    
             The "unsigned" modifier may be used to declare a symbol  as  an
          unsigned positive only value. Note that unlike some 'C' compilers,
          this modifier may be applied to a character (8 bit) variable.
    
                            eg: unsigned char count;

    MICRO-C                                                          Page: 8


             The "extern" modifier causes the compiler to be  aware  of  the
          existance and  type  of  a  global  symbol,  but  not  generate  a
          definition for that symbol. This allows the module being  compiled
          to reference a symbol which is defined  in  another  module.  This
          modifier may not be used with local symbols.
    
                            eg: extern char getc();
    
             A  symbol  declared  as  external  may  be  re-declared  as   a
          non-external at a later  point  in  the  code,  in  which  case  a
          definition for it will be generated. This allows  "extern"  to  be
          used to inform the compiler of a function or variable type so that
          it can be referenced  properly  before  that  symbol  is  actually
          defined.
    
             The "static" modifier causes global  symbols  to  be  available
          only in the file where they are defined.  Variables  or  functions
          declared  as  "static"  will  not  be   accessable   as   "extern"
          declarations in other object files, nor will they cause  conflicts
          with duplicate names in those files.
    
                         eg: static int variable_name;
    
             When applied to local symbols,  the  "static"  modifier  causes
          those variables to be allocated in  a  reserved  area  of  memory,
          instead of on the processor stack. This has the  effect  that  the
          contents of the variable will be retained  between  calls  to  the
          function. It also means that the variable  may  be  initialzed  at
          compile time.
    
             The "register" modifier indicates to the  code  generator  that
          this is a high priority variable, and should be kept where  it  is
          easy to get at. Since  its  interpretation  depends  on  the  code
          generator, it is often  ignored  in  simple  implementations.  See
          "Functions" for a  special  use  of  "register"  when  defining  a
          function.
    
                          eg: register unsigned count;
    
             Symbols declared with a preceeding '*' are assumed to be 16 bit
          pointers to the declared type.
    
                             eg: int *pointer_name;
    
             Symbol names declared followed by square brackets  are  assumed
          to be arrays with a number of dimensions equal to  the  number  of
          '[]' pairs that follow. The size of each dimension  is  identified
          by a constant value  contained  within  the  corresponding  square
          brackets.
    
                          eg: char array_name[5][10];

    MICRO-C                                                          Page: 9


          3.2.1 Global Symbols
    
                Symbols  declared  outside  of  a  function  definition  are
             considered to  be  global  and  will  have  memory  permanently
             reserved for them. Global symbols are defined by  name  in  the
             output file, allowing other modules to access them.
    
                Note that the compiler IS case  sensitive,  however  if  the
             assembler you are using is NOT, you  must  be  careful  not  to
             declare any global symbols with names that differ only in case.
    
                All non-initialized global variables are  generated  at  the
             very end of the output file, after the literal pool is  dumped.
             Since non-initialized globals do not generate object code, this
             allows them to be excluded from the image file when it is saved
             to disk.
    
                Global variables may be initialized with one or more values,
             which are expressed as a single array of  integers  REGUARDLESS
             of the size and shape of the variable. If more than  one  value
             is expressed, '{' and '}' must be used.
    
                   eg: int i = 10, j[2][2] = { 1, 2, 3, 4 };
    
                When arrays are declared, a null dimension may  be  used  as
             the dimension size, in which case the size of  the  array  will
             default to the number of initialized values.
    
                         eg: int array[] = { 1, 2, 3 };
    
                Initialized global variables are automatically saved  within
             the code image,  insuring  that  the  initial  values  will  be
             available at run time. Any non-initialized elements of an array
             which has been partly initialized will be set to zero.
    
                Non-initialized global variables are not preset in any  way,
             and will be undefined at the beginning of program execution.
    
          3.2.2 Local Symbols
    
                Symbols declared within a function definition are  allocated
             on the stack, and  exist  only  during  the  execution  of  the
             function.
    
                To simplify the allocation and de-allocation of stack space,
             all local symbols must be declared  at  the  beginning  of  the
             function before any code producing statements are encountered.
    
                MICRO-C does not support initialization of non-static  local
             variables in the declaration statement. Since  local  variables
             have to be initialized every time the function is entered,  you
             can get the same effect  using  assignment  statements  at  the
             beginning of the function.
    
                No type is assumed for  arguments  to  functions.  Arguments
             must be explicitly declared, otherwise they will  be  undefined
             within the scope of the function definition.

    MICRO-C                                                          Page: 10


          3.2.3 More Symbol Examples
    
            /* Global variables are defined outside of any function */
            char a;                     /* 8 bit signed */
            unsigned char b;            /* 8 bit unsigned */
            int c;                      /* 16 bit signed */
            unsigned int d;             /* 16 bit unsigned */
            unsigned e;                 /* also 16 bit unsigned */
            extern char f();            /* external function returning char */
            static int g;               /* 16 bit signed, local to file */
            int h[2] = { 1, 2 };        /* initialized array (2 ints) */
    
            main(a, b)                  /* "int" function containing code */
            /* Function arguments are defined between function name and body */
                int a;                  /* 16 bit signed */
                unsigned char *b;       /* pointer to 8 bit unsigned */
            {
            /* Local variables are defined inside the function body */
            /* Note that in MICRO-C, only "static" locals can be initialized */
                unsigned c;             /* 16 bit unsigned */
                static char d[5];       /* 8 bit signed, reserved in memory */
                static int e = 1;       /* 16 bit signed, initial value is 1 */
            /* Function code goes here ... */
                c = 0;                  /* Initialize 'c' to zero */
                strcpy(d, "Name");      /* Initialize 'd' to "name" */
            }
    
       3.3 Arrays & Pointers
    
             When MICRO-C passes an array to a function, it actually  passes
          a POINTER to the array. References to arrays which  are  arguments
          are automatically performed through the pointer.
    
             This allows the use of pointers and arrays to be interchangable
          through the context of a function call. Ie: An array passed  to  a
          function may be declared and used as  a  pointer,  and  a  pointer
          passed to a function may be declared and used as an array.

    MICRO-C                                                          Page: 11


       3.4 Functions
    
             Functions are  essentially  initialized  global  symbols  which
          contain executable code.
    
             MICRO-C accepts  any  valid  value  as  a  function  reference,
          allowing  some  rather  unique  (although  non-standard)  function
          calls.
    
          For example:
    
                function();     /* call function */
                variable();     /* call contents of a variable */
                (*var)();       /* call indirect through variable */
                (*var[x])();    /* call indirect through indexed array */
                0x5000();       /* call address 0x5000 */
    
             MICRO-C accepts both the  "classic"  and  "modern"  formats  of
          argument definition for a function.
    
             In the "classic" format, only the argument names are placed  in
          the brackets following the function name. The closing  bracket  is
          followed by formal declarations for the arguments (in any order):
    
              eg: int function(a, b, c) int a, c; char b; { ... }
    
             If the "modern" format, complete declarations for EACH argument
          are enclosed in the brackets following the function name:
    
                 eg: int function(int a, char b, int c) { ... }
    
             Since this is a single pass compiler, operands to functions are
          evaluated and pushed on the stack in the order in which  they  are
          encountered, leaving the last operand closest to the  top  of  the
          stack. This is the opposite order from which  many  'C'  compilers
          push operands.
    
             For functions with a fixed number of arguments,  the  order  of
          which operands  are  passed  is  of  no  importance,  because  the
          compiler looks after generating  the  proper  stack  addresses  to
          reference variables.  HOWEVER,  functions  which  use  a  variable
          number of arguments are affected for two reasons:
    
          1) The location of the LAST arguments are known (as fixed  offsets
             from the stack pointer) instead of the FIRST.
    
          2) The symbols defined as arguments  in  the  function  definition
             represent the LAST arguments instead of the FIRST.
    
             If a function is declared as "register", it  serves  a  special
          purpose and causes the accumulator to be loaded with the number of
          arguments passed whenever the function is called. This allows  the
          function to know how many  arguments  were  passed  and  therefore
          determine the location of the first argument.

    MICRO-C                                                          Page: 12


       3.5 Structures & Unions
    
             Combinations of other variable  types  can  be  organized  into
          STRUCTURES or UNIONS, which allow them  to  be  manipulated  as  a
          single entity.
    
             In a structure, the  individual  items  occur  sequentially  in
          memory, and the total size of the structure  is  the  sum  of  its
          elements. Structures are usually  used  to  create  "records",  in
          which related items are grouped together. An array  of  structures
          is the common method of implementing an "in-memory" database.
    
             A union is similar to a structure, except that  the  individual
          items are overlaid in memory, and the total size of the  union  is
          the size of its largest element. Unions are usually used to  allow
          a single block of memory to be accessed as different 'C'  variable
          types. An example of this would be in handling a message  received
          in memory, in which a "type" byte indicates how the  remainder  of
          the message data should be interpreted.
    
             Here are some example of how structures are  defined  and  used
          (unions are defined and used in an identical manner,  except  that
          the word 'union' is substituted for 'struct'):
    
            /* Create structure named 'data' with 'a,b,c & d' as members */
            struct {
                int a;
                int b;
                char c;
                char d; } data;
    
            /* Create structure template named 'mystruc'... */
            /* No actual structure variable is defined */
            struct mystruc {
                int a;
                int b;
                char c;
                char d; };
    
            /* Create structure named 'data' using above template */
            struct mystruc data;
    
            /* Create structure template 'mystruc', AND define a */
            /* structure variable named 'data' */
            struct mystruc {
                int a;
                int b;
                char c;
                char d; } data;

    MICRO-C                                                          Page: 13


            /* Create an array of structures, a pointer to a structure */
            /* and an array of pointers to a structure *
            struct mystruct array[10], *pointer, *parray[10];
    
            /* To set value in structure variable/members */
            data.a = 10;            /* Direct access */
            array[1].b = 10;        /* Direct array access */
            pointer->c = 'a';       /* Pointer access */
            parray[2]->d = 'b';     /* Pointer array access */
    
            /* To read value in structure variable/members */
            value = data.a;         /* Direct access */
            value = data[1].b;      /* Direct array access */
            value = pointer->c;     /* Pointer access */
            value = parray[2]->d;   /* Pointer array access */
    
          3.5.1 Notes on MICRO-C structure implementation:
    
                Structures and Unions as implemented in MICRO-C are  similar
             to the implementation of the original UNIX  'C'  compiler,  and
             are bound by similar limitations, as  well  as  a  few  MICRO-C
             specific ones.  Here  is  a  list  of  major  differences  when
             compared to a modern ANSI compiler:
    
                All structure and member names MUST  be  unique  within  the
             scope of the definition. A special case  exists,  where  common
             member names may be used in  multiple  structure  templates  if
             they have EXACTLY the same type and offset into the  structure.
             This also saves symbol table memory, since only one copy of the
             member definition is actually kept.
    
                MICRO-C does NOT pass entire structures to functions on  the
             stack. Like  arrays,  MICRO-C  passes  structures  by  ADDRESS.
             Structure variables which are function arguments  are  accessed
             through pointers. For source code compatibility with  compilers
             which do pass the entire structure, if you declare the argument
             as a direct (non-pointer) structure, the direct ('.')  operator
             is used to dereference it, even though it is actually a pointer
             reference.
    
                If you  MUST  have  a  local  copy  of  the  structure,  use
             something like:
    
                func(sptr)
                    struct mystruc *sptr;
                {
                    struct mystruc data;
                    memcpy(data, sptr, sizeof(data));
                    ...
                }

    MICRO-C                                                          Page: 14


                To obtain the size of a structure from  its  template  name,
             use the 'struct'  keyword  in  conjunction  with  the  'sizeof'
             operator.   In   the   above   example,   you   could   replace
             'sizeof(data)' with 'sizeof(struct mystruc)'.
    
                To obtain the size of a structure member, you  must  specify
             it in the context of a structure reference with another symbol:
    
              sizeof(variable.member) or sizeof(variable->member)
    
                NOTE: The current compiler allows almost any symbol  to  the
             left of the '.' or '->' operator in a 'sizeof', however  future
             versions of the compiler may insist on a structure variable  or
             a pointer to structure variable.
    
                Pointers to structures are internally stored as pointers  to
             'char', and therefore will only increment/decrement by  1  when
             ++/-- is used. To advance a pointer by the size of a structure,
             use:
    
                         ptr += sizeof(struct mystruc)
    
                The 'struct' and 'union' keywords  are  not  accepted  in  a
             TYPECAST. This is most commonly used to setup a  pointer  to  a
             structure. Since MICRO-C stores its pointers to  structures  as
             pointers to char, you can use (char*) as the typecast, and  get
             the same functionality.
    
                A structure name by itself (without  '.member')  acts  in  a
             manner similar to a character array name.  With  no  operation,
             the address of the structure is returned. You can also use '[]'
             to access  individual  bytes  in  the  structure  by  indexing,
             although doing so is highly non-portable.
    
                MICRO-C allows static or global structures to be initialized
             in the declaration, however the initial values are read  as  an
             array of bytes, and are assigned directly to  structure  memory
             without regard for the type or size of its members:
    
                struct mystruc data = { 0, 1, 0, 2, 3, 4 };
                /* A=0:1, B=0:2, C=3, D=4 */
    
                You can use INT and CHAR to switch back  and  forth  between
             word/byte initialization within the value list:
    
                struct mystruct data = { int 0, 1, char 2, 3 };
                /* A=0, B=1, C=2, D=3 */
    
                MICRO-C does not WORD ALIGN structure elements. When using a
             processor which requires word alignment, it is the  programmers
             responsibility to maintain alignment, using filler  bytes  etc.
             when necessary.

    MICRO-C                                                          Page: 15


       3.6 Control Statements
    
             The following control statements are implemented in MICRO-C:
    
                if(expression)
                    statement;
    
                if(expression)
                    statement;
                else
                    statement;
    
                while(expression)
                    statement;
    
                do
                    statement;
                while expression;
    
                for(expression; expression; expression)
                    statement;
    
                return;
    
                return expression;
    
                break;
    
                continue;
    
                switch(expression) {
                    case constant_expression :
                        statement;
                        ...
                        break;
                    case constant_expression :
                        statement;
                        ...
                        break;
                        .
                        .
                        .
                    default:
                        statement; }
    
                label: statement;
    
                goto label;
    
                asm "...";
    
                asm {
                    ...
                    }

    MICRO-C                                                          Page: 16


    3.6.1 Notes on Control Structures
    
        1)  Any "statement" may be a single statement or a compound
            statement enclosed within '{' and '}'.
    
        2)  All three "expression"s in the "for" command are optional.
    
        3)  If a "case" selection does not end with "break;", it will
            "fall through" and execute the following case as well.
    
        4)  Expressions following 'return' and 'do/while' do not have
            to be contained in brackets (although this is permitted).
    
        5)  Label names may preceed any statement, and must be any
            valid symbol name, followed IMMEDIATELY by ':' (No spaces
            are allowed). Labels are considered LOCAL to a function
            definition and will only be accessable within the scope
            of that function.
    
        6)  The 'asm' statement used to implement the inline assembly
            language capability of MICRO-C accepts two forms:
                asm "...";      <- Assemble single line.
                asm {           <- Assemble multiple lines.
                    ...
                    }

    MICRO-C                                                          Page: 17


       3.7 Expression Operators
    
             The following expression operators are implemented in MICRO-C:
    
    3.7.1 Unary Operators
    
        -           - Negate
        ~           - Bitwise Complement
        !           - Logical complement
        ++          - Pre or Post increment
        --          - Pre or post decrement
        *           - Indirection
        &           - Address of
        sizeof      - Size of a object or type
        (type)      - Typecast
    
    3.7.2 Binary Operators
    
        +           - Addition
        -           - Subtraction
        *           - Multiplication
        /           - Division
        %           - Modulus
        &           - Bitwise AND
        |           - Bitwise OR
        ^           - Bitwise EXCLUSIVE OR
        <<          - Shift left
        >>          - Shift right
        ==          - Test for equality
        !=          - Test for inequality
        >           - Test for greater than
        <           - Test for less than
        >=          - Test for greater than or equal to
        <=          - Test for less than or equal to
        &&          - Logical AND
        ||          - Logical OR
        =           - Assignment
        +=          - Add to self assignment
        -=          - Subtract from self assignment
        *=          - Multiply by self assignment
        /=          - Divide by and reassign assignment
        %=          - Modular self assignment
        &=          - AND with self assignment
        |=          - OR with self assignment
        ^=          - EXCLUSIVE OR with self assignment
        <<=         - Shift left self assignment
        >>=         - Shift right self assignment

    MICRO-C                                                          Page: 18


    NOTES:
    
        1)  The expression "a && b" returns 0 if "a" is zero, otherwise the
            value of "b" is returned. The "b" operand is NOT evaluated if
            "a" is zero.
    
        2)  The expression "a || b" returns the value of "a" if it is not 0,
            otherwise the value of "b" is returned. The "b" operand is NOT
            evaluated if "a" is non-zero.
    
    3.7.3 Other Operators
    
        ;           - Ends a statement.
        ,           - Allows several expressions in one statement.
                    + Separates symbol names in multiple declarations.
                    + Separates constants in multi-value initialization.
                    + Separates operands in function calls.
        ?           - Conditional expression (ternary operator).
        :           - Delimits labels, ends CASE and separates conditionals.
        .           - Access a structure member directly.
        ->          - Access a structure member through a pointer.
        { }         - Defines a BLOCK of statements.
        ( )         - Forces priority in expression, indicates function calls.
        [ ]         - Indexes arrays. If fewer index values are given than the
                      number of dimensions which are defined for the array,
                      the value returned will be a pointer to the appropriate
                      address.
    
                    Eg:
                        char a[5][2];
    
                        a[3] returns address of forth row of two characters.
                        (remember index's start from zero)
    
                        a[3][0] returns the character at index [3][0];

    MICRO-C                                                          Page: 19


       3.8 Inline Assembly Language
    
             Although 'C' is a powerful and  flexible  language,  there  are
          sometimes instances where a particular operation must be  peformed
          at the assembly language level. This most  often  involves  either
          some processor feature for which there  is  no  corresponding  'C'
          operation, or a section of very time critical code.
    
             MICRO-C provides access to assembly  language  with  the  'asm'
          statement, which has two basic forms. The first is:
    
                                  asm "..." ;
    
             In this form, the entire  text  contained  between  the  double
          quote characters (") is output as a single line to the  assembler.
          Note that a  semicolon  is  required,  just  like  any  other  'C'
          statement.
    
             Since this is a standard 'C' string, you can  use  any  of  the
          "special" characters, and thus you could output multiple lines  by
          using '\n' within the string. Another important characteristic  of
          it being a string is that it will be protected from  pre-processor
          substitution.
    
             The second form of the 'asm' statement is:
    
                                     asm {
                                      ...
                                       }
    
             In this form, all lines between '{' and '}' are output  to  the
          assembler. Any text following the opening '{' (on the  same  line)
          is ignored. Due to  the  unknown  characteristics  of  the  inline
          assembly code, the closing '}' will only be recognized when it  is
          the first non-whitespace character on a line.
    
             The integral pre-processor will not perform substitution on the
          inline assembly code, however  the  external  pre-processor  (MCP)
          will substitute in this form. This allows you to  create  assembly
          language "macros" using MCP, and have parameters substituted  into
          them when they are expanded:
    
            /*
             * This macro issues a 'SETB' instruction for its parameter
             */
            #define setbit(bit) asm {\
                SETB bit\
            }
    
            /*
             * This macro WILL NOT WORK, since the 'bit' operand to the SETB
             * instruction is contained within a string and is therefore
             * protected from substitution by the pre-processor
             */
            #define setbit(bit) asm " SETB bit";

    MICRO-C                                                          Page: 20


       3.9 Preprocessor Commands
    
             The  MICRO-C  compiler  supports  the  following  pre-processor
          commands. These commands are recognized only if they occur at  the
          beginning of the input line.
    
             NOTE:  This  describes  the  limited  pre-processor  which   is
          integral to the  compiler,  see  also  the  section  on  the  more
          powerful external processor (MCP).
    
          3.9.1 #define <name> <replacement_text>
    
                The "#define" command allows a global name  to  be  defined,
             which will be replaced with the indicated text whenever  it  is
             encountered in the input file. This occurs prior to  processing
             by the compiler.
    
          3.9.2 #file <filename>
    
                Sets the filename of the currently  procssing  file  to  the
             given  string.  This  command   is   used   by   the   external
             pre-processor (MCP) to insure that error messages indicate  the
             original source file.
    
          3.9.3 #include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "#include" in the original file.
    
          3.9.4 #ifdef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is defined.
    
          3.9.5 #ifndef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is NOT defined.
    
          3.9.6 #else
    
                Processes the following lines (up to  #endif)  only  if  the
             preceeding #ifdef or #ifndef was false.
    
          3.9.7 #endif
    
                Terminates #ifdef and #ifndef
    
                NOTE: The integral pre-processor does not support nesting of
             the #ifdef and #idndef constructs. If you wish  to  nest  these
             conditionals, you must use the external pre-processor (MCP).

    MICRO-C                                                          Page: 21


       3.10 Error Messages
    
             When MICRO-C detects an  error,  it  outputs  an  informational
          message indicating the type of problem encountered.
    
             The error message is preceeded by the filename and line  number
          where the error occured:
    
                           program.c(5): Syntax error
    
             In the above example, the error occured in the file "program.c"
          at line 5.
    
             The following error messages are produced by the compiler:
    
          3.10.1 Compilation aborted
    
                The preceeding error was so severe than the compiler  cannot
             proceed.
    
          3.10.2 Constant expression required
    
                The compiler requires a constant  expression  which  can  be
             evaluated at compile time (ie: no variables).
    
          3.10.3 Declaration must preceed code.
    
                All local variables must be defined at the beginning of  the
             function, before any code producing statements are processed.
    
          3.10.4 Dimension table exhausted
    
                The compiler has encountered more  active  array  dimensions
             than it can handle.
    
          3.10.5 Duplicate local: 'name'
    
                You have declared the named  local  symbol  more  than  once
             within the same function definition.
    
          3.10.6 Duplicate global: 'name'
    
                You have declared the named global symbol more than once.
    
          3.10.7 Expected '<token>'
    
                The compiler  was  expecting  the  given  token,  but  found
             something else.
    
          3.10.8 Expression stack overflow
    
                The compiler has found a more complicated expression than it
             can handle. Check that it is of  correct  syntax,  and  if  so,
             break it up into two simpler expressions.

    MICRO-C                                                          Page: 22


          3.10.9 Expression stack underflow
    
                The compiler has made an error in  parsing  the  expression.
             Check that it is of correct syntax.
    
          3.10.10 Illegal indirection
    
                You have attempted to perform an indirect operation ('*'  or
             '[]') on an entity which is not a pointer or array. This  error
             will also result if you attempt to index  an  array  with  more
             indices than it has dimensions.
    
          3.10.11 Illegal initialization
    
                Local variables may not be initialized  in  the  declaration
             statement. Use assignments at the  beginning  of  the  function
             code to perform the initialization.
    
          3.10.12 Illegal nested function
    
                You may not declare a  function  within  the  definition  of
             another function.
    
          3.10.13 Improper type of symbol: 'name'
    
                The named  symbol  is  not  of  the  correct  type  for  the
             operation that you are attempting. Eg: 'goto' where the  symbol
             is not a label.
    
          3.10.14 Improper #else/#endif
    
                A #else or #endif statement is out of place.
    
          3.10.15 Inconsistant member offset: 'name'
    
                The named structure member is multiply defined,  and  has  a
             different offset from its first definition.
    
          3.10.16 Inconsistant member type: 'name'
    
                The named structure member is multiply defined,  and  has  a
             different type from its first definition.
    
          3.10.17 Inconsistant re-declaration: 'name'
    
                You have attempted to redefine  the  named  external  symbol
             with a type which does not match its previously declared type.
    
          3.10.18 Incorrect declaration
    
                A statement occuring outside of a function definition is not
             a valid declaration for a function or global variable.

    MICRO-C                                                          Page: 23


          3.10.19 Invalid '&' operation
    
                You have attempted to reference  the  address  of  something
             that has no address. This error also occurs when you attempt to
             take the address of an array without giving it a  full  set  of
             indicies. Since the address is already returned in  this  case,
             simply drop the '&'. (The error occurs because you  are  trying
             to take the address of an address).
    
          3.10.20 Macro expansion too deep
    
                The compiler has encountered a nested macro reference  which
             is too deep to be resolved.
    
          3.10.21 Macro space exhausted
    
                The compiler has encountered  more  macro  ("#define")  text
             than it has room to store.
    
          3.10.22 No active loop
    
                A "continue" or "break" statement was  encountered  when  no
             loop is active.
    
          3.10.23 No active switch
    
                A "case" or "default"  statement  was  encountered  when  no
             "switch" statement is active.
    
          3.10.24 Not an argument: 'name'
    
                You have declared the named variable as an argument, but  it
             does not appear in the argument list.
    
          3.10.25 Non-assignable
    
                You have attempted an operation which results in  assignment
             of a value to an entity which cannot be assigned. (eg: 1 = 2);
    
          3.10.26 Numeric constant required
    
                The compiler requires a constant expression which returns  a
             simple numeric value.
    
          3.10.27 String space exhausted
    
                The compiler has encountered more literal  strings  than  it
             has room store.
    
          3.10.28 Symbol table full
    
                The compiler has encountered more symbol definitions than it
             can handle.

    MICRO-C                                                          Page: 24


          3.10.29 Syntax error
    
                The statement shown does not follow syntax rules and  cannot
             be parsed.
    
          3.10.30 Too many active cases
    
                The compiler has run out of space  for  storing  switch/case
             tables. Reduce the number of active "cases".
    
          3.10.31 Too many defines
    
                The compiler has encountered more '#define' statements  than
             it can handle. Reduce the number of #defines.
    
          3.10.32 Too many errors
    
                The compiler is aborting because of excessive errors.
    
          3.10.33 Too many includes
    
                The compiler has encountered more  nested  "#include"  files
             than it can handle.
    
          3.10.34 Too many initializers
    
                You have specified more initialization values than there are
             locations in the global variable.
    
          3.10.35 Type clash
    
                You have attempted to use a  value  in  a  manner  which  is
             inconsistant with its typing information.
    
          3.10.36 Unable to open: 'name'
    
                A "#include" command specified the named file,  which  could
             not be opened.
    
          3.10.37 Undefined: 'name'
    
                You have referenced a name which is not defined as  a  local
             or global symbol.
    
          3.10.38 Unknown structure/member: 'name'
    
                You have referenced a  structure  template  or  member  name
             which is not defined.
    
          3.10.39 Unreferenced: 'name'
    
                The named  symbol  was  defined  as  a  local  symbol  in  a
             function, but was never used in that function. This error  will
             occur at the end of  the  function  definition  containing  the
             symbol declaration. It is only a warning, and  will  not  cause
             the compile to abort.

    MICRO-C                                                          Page: 25


          3.10.40 Unresolved: 'name'
    
                The named symbol was forward  referenced  (Such  as  a  GOTO
             label), and was never defined. This error will occur at the end
             of the function definition containing the reference.
    
          3.10.41 Unterminated conditional
    
                The end of file was encountered  when  a  "#if"  or  "#else"
             conditional block was being processed.
    
          3.10.42 Unterminated function
    
                The  end  of  the  file  was  encountered  when  a  function
             definition was still open.

    MICRO-C                                                          Page: 26


       3.11 Quirks
    
             Due  to  its  background  as  a  highly  compact  and  portable
          compiler, and its target application in embedded systems,  MICRO-C
          deviates from standard 'C' in  some  areas.  The  following  is  a
          summary of the major infractions and quirks:
    
             When using the INTERNAL  pre-processor,  the  operands  to  '#'
          commands are parsed based on separating spaces, and any portion of
          the line not required is ignored.  In  particular,  the  '#define'
          command only accepts a definition up to  the  next  space  or  tab
          character.
    
            eg: #define APLUSONE A+1        <-- uses "A+1"
                #define APLUSONE A +1       <-- uses "A"
    
             Comments are stripped by the token scanner, which occurs  AFTER
          the '#' commands are processed.
    
            eg: #define NULL    /* comment */   <-- uses "/*"
    
             Note that since comments can therefore be included in "#define"
          symbols, you can use "/**/" to simulate spaces between tokens.
    
            eg: #define BYTE unsigned/**/char
    
             Include filenames are not delimited by '""'  or  '<>'  and  are
          passed to the operating system exactly as entered.
    
            eg: #include \mc\stdio.h
    
             NOTE:  The  above  quirks  DO  NOT  APPLY  when  the   EXTERNAL
          pre-processor (MCP) is used.
    
             The appearance of a variable name in the argument  list  for  a
          function  declaration  serves  only  to  identify  that  variables
          location on the stack. MICRO-C will not define the variable unless
          it is explicitly declared (between the argument list and the  main
          function body). In other words, all arguments to a  function  must
          be explicitly declared.
    
             MICRO-C is more  strict  about  its  handling  of  the  ADDRESS
          operator ('&') than most other compilers. It will produce an error
          message if you attempt to take the address of  a  value  which  is
          already a fixed address (such as an array name without a full  set
          of indicies). Since an address is already produced in such  cases,
          simply drop the '&'.
    
             The 'x' in '0x' and '\x' is accepted in lower case only.

    MICRO-C                                                          Page: 27


             When operating on pointers, MICRO-C only scales  the  increment
          (++), decrement (--) and index ([]) operations to account for  the
          size of the pointer:
    
            eg: char *cptr;     /* pointer to character */
                int  *iptr;     /* pointer to integer */
                ++cptr;         /* Advance one character */
                ++iptr;         /* Advance one integer */
                cptr[10];       /* Access the tenth character */
                iptr[10];       /* Access the tenth integer */
                cptr += 10;     /* Advance 10 characters */
                iptr += 10;     /* Advance ONLY FIVE integers */
    
            NOTE: A portable way to advance "iptr" by integers is:
    
                iptr = &iptr[10];   /* Advance 10 integers */
    
             Since  structures  are  internally  represented  as  arrays  of
          "char", incrementing a pointer to a structure  will  advance  only
          one (1) byte in memory. To advance to the "next" instance  of  the
          structure, use:
    
                        ptr += sizeof(struct template);
    
             The INDEXING operator '[]' is not commutative  in  MICRO-C.  In
          other words 'array[index]' cannot be expressed as 'index[array]'.
    
             MICRO-C does  not  support  "complex"  declarations  which  use
          brackets '()' for other than function parameters. These  are  most
          often used in establishing pointers to functions:
                    int (*a)();     /* Pointer to function returning INT */
                    (*a)();         /* Call address in 'a' */
    
             Since MICRO-C allows you to call any value by following it with
          '()', you can get  the  desired  effect  in  the  above  case,  by
          declaring 'a' as a simple pointer to int, and calling it with  the
          same syntax:
                    int *a;         /* Pointer to INT */
                    (*a)();         /* Call address in 'a' */
    
             MICRO-C will not output external  declarations  to  the  output
          file  for  any  variables  or  functions  which  are  declared  as
          "extern", unless that symbol is actually  referenced  in  the  'C'
          source code. This prevents "extern" declarations in system  header
          files (such as "stdio.h") which are used as  prototypes  for  some
          library functions from causing those functions to be  loaded  into
          the  object  file.  Therefore,  any  "extern"  symbols  which  are
          referenced only by inline assembly code must be  declared  in  the
          assembly code, not by the MICRO-C "extern" statement.

    MICRO-C                                                          Page: 28


             Unlike some  'C'  compilers,  MICRO-C  will  process  character
          expressions using only  BYTE  values.  Character  values  are  not
          promoted to INT unless there is  an  INT  value  involved  in  the
          expression. This results in much more efficent code  when  dealing
          with characters, particularily  on  small  processors  which  have
          limited 16 bit instructions. Consider the statement:
    
                                 return c + 1;
    
             On some compilers, this will sign extend the character variable
          'c' into an integer value, and then ADD an integer  1  and  return
          the  result.  MICRO-C  will  ADD  the  character  variable  and  a
          character 1, and then promote the result to INT  before  returning
          it (results of expressions as  operands  to  'return'  are  always
          promoted to int).
    
             Unfortunately, programs have been written  which  rely  on  the
          automatic promotion of characters to INTs to  work  properly.  The
          most common source of problems is code  which  attempts  to  treat
          CHAR variables as UNSIGNED values (many older  compilers  did  not
          support UNSIGNED CHAR). For example:
    
                                return c & 255;
    
             In a compiler which always evaluates character  expressions  as
          INT, the above statement will extract the value of 'c' as positive
          integer ranging from 0 to 255.
    
             In MICRO-C, ANDing a character with 255  results  in  the  same
          character, which gets promoted to an integer  value  ranging  from
          -128 to 127. To force the promotion  within  the  expression,  you
          could CAST the variable to an INT:
    
                              return (int)c & 255;
    
             The same objective can be achieved  in  a  more  efficent  (and
          correct) manner by declaring the variable 'c' as UNSIGNED CHAR, or
          by CASTing the variable to an UNSIGNED value:
    
                              return (unsigned)c;
    
             Note that this is not only more clearly shows the intent of the
          programmer, but also results is more efficent code generated.

    MICRO-C                                                          Page: 29


             A related quirk arises because most processors do not support a
          simple efficent method for adding or subtracting a  SIGNED  8  bit
          quantity and a 16 bit quantity. The code generators supplied  with
          MICRO-C make the assumption that character values being  added  or
          subtracted to/from integers will contain only POSITIVE values, and
          thus use UNSIGNED  addition/subtraction.  This  allows  much  more
          efficent code to be generated, as the carry/borrow  from  the  low
          order byte of the operation is simply propagated to the high order
          byte of the result (an operation  supported  in  hardware  by  the
          CPU).
    
             For those rare instances where you do wish  to  add/subtract  a
          potentially negative character value to/from an int, you can force
          the expression to be performed  in  less  efficent  fully  16  bit
          arithmetic by casting the character to an int.
    
                int i;
                char c;
                ...
                i += c;         /* Very efficent... C should be positive */
                i += (int)c;    /* Less efficent... C can be negative */
    
             Read the notes at the end of the section  entitled  "Structures
          and Unions" for information on  limitations  or  differences  from
          standard 'C' in MICRO-C's implementation of structures and unions.

    MICRO-C                                                          Page: 30


    4. ADVANCED TOPICS
    
          This section provides information on the more advanced aspects  of
       MICRO-C, which  is  generally  not  needed  for  casual  use  of  the
       language.
    
       4.1 Conversion Rules
    
             MICRO-C keep track of the "type" of  each  value  used  in  all
          expressions. This type identifies certain characteristics  of  the
          value,  such  as   size   range   (8/16   bits),   numeric   scope
          (signed/unsigned), reference (value/pointer) etc.
    
             When an  operation  is  performed  on  two  values  which  have
          identical "types", MICRO-C assigns that same "type" to the result.
    
             When the  two  value  "types"  involved  in  an  operation  are
          different, MICRO-C calculates the "type" of the result  using  the
          following rules:
    
          4.1.1 Size range
    
                If both values are  direct  (not  pointer)  references,  the
             result will be 8 bits only if  both  values  were  8  bits.  If
             either value was 16 bits, the result will be 16 bits.
    
                If one value is a pointer, and  the  other  is  direct,  the
             result will be a pointer to the same size value as the original
             pointer.
    
                If both values were pointers, the result will be  a  pointer
             to 16 bits only if both original  pointers  referenced  16  bit
             values. If either pointer referenced an 8 bit value, the result
             will reference an 8 bit value.
    
          4.1.2 Numeric Scope
    
                The result of an expression is considered to be signed  only
             if both original values were signed. If  either  value  was  an
             unsigned value, the result is unsigned.
    
          4.1.3 Reference
    
                If either of the original values was a pointer,  the  result
             will be a pointer.
    
             Note that this "calculated" result type  is  used  for  partial
          results within an expression. Whenever a symbol such as a variable
          or function is referenced, the type of that symbol is  taken  from
          its declaration, no matter what "type" of value  was  last  stored
          (variable) or returned (function).
    
             The TYPECAST  operation  may  be  used  to  override  the  type
          calculated for the result of an expression if necessary.

    MICRO-C                                                          Page: 31


       4.2 Assembly Language Interface
    
             Assembly language programs may be called from 'C' functions and
          vice versa. These programs may be in the form of  inline  assembly
          language statements in the 'C' source code, or  separately  linked
          modules.
    
             When MICRO-C calls any routine ('C'  or  assembler),  it  first
          pushes all arguments to the routine onto the processor  stack,  in
          the order in  which  they  occur  in  the  argument  list  to  the
          function. This means that the LAST argument  to  the  function  is
          LOWEST on the processor stack.
    
             Arguments are always pushed as 16 bit values. Character  values
          are extended to 16 bits, and arrays are passed as 16 bit  pointers
          to the array. (MICRO-C knows that arrays which are  arguments  are
          actually  pointers,  and  automatically  references  through   the
          pointer).
    
             After pushing the arguments, MICRO-C then generates  a  machine
          language subroutine  call,  thereby  executing  the  code  of  the
          routine.
    
             Since the compiler uses the ACCUMULATOR and INDEX REGISTER,  it
          will automatically save them (if necessary) during  processing  of
          the arguments to the function (even if no arguments are  present),
          and therefore these registers do not have to be preserved  by  the
          called routine.
    
             NOTE that any other  registers  used  by  the  code  generation
          routines (register variables etc) will not be  saved  by  MICRO-C,
          and should be preserved by called functions if their content is to
          be relied on between function calls.
    
             Once the called routine returns, the arguments are removed from
          the stack by the calling program. This usually consists of  simply
          adding the number of  bytes  pushed  as  arguments  to  the  stack
          pointer.
    
             When the called function executes, the first thing usually done
          is to push any registers which must be preserved, and  to  reserve
          space on the stack for any local variables which are required.  In
          some implementations, a "base" register may also be established to
          provide a stable reference to the local variables and arguments.
    
             It is the responsibility of the called function to  remove  any
          saved registers and local variable space from the stack before  it
          returns. If a value is to be returned to the calling  program,  it
          is expected to be in the ACCUMULATOR register.

    MICRO-C                                                          Page: 32


             Local variables in a  function  may  be  referenced  as  direct
          offsets from the "base" register or stack pointer.  Note  that  if
          the stack pointer is used, offsets must be adjusted for the number
          of bytes which are pushed and  popped  on  the  stack  during  the
          execution of the function.
    
             The address of a particular local variable is calculated as:
    
                                "base register"
                                       -
                     (Size of all local variables in bytes)
                                       + 
               (size of all preceeding local variables in bytes)
    
                                    -- OR --
    
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
               (size of all preceeding local variables in bytes)
    
             Arguments to a  function  may  also  be  referenced  as  direct
          offsets from the "base" register or stack  pointer,  in  much  the
          same way as local variables are.
    
             The address of a particular argument is calculated as:
    
                                "base register"
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
                                       +
                      (# arguments from LAST argument) * 2
    
                                    -- OR --
    
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
                     (size of all local variables in bytes)
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
                                       +
                      (# arguments from LAST argument) * 2
    
             NOTE: The (number of bytes pushed at entry of  function)  is  a
          function of the code generator,  and  depends  on  the  particular
          MICRO-C implementation. Examine  some  assembly  output  from  the
          compiler to determine the actual number on your system.

    MICRO-C                                                          Page: 33


             If a function has been declared  as  "register",  MICRO-C  will
          load the accumulator with  the  number  of  arguments  which  were
          passed, each time the function is called. This allows the function
          to determine the location of the first argument.
    
             The address of  the  first  argument  passed  to  a  "register"
          function may be calculated as:
    
                           (accumulator contents) * 2
                                       + 
                                "base register"
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
    
                                    -- OR --
    
                           (accumulator contents) * 2
                                       +
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
                     (size of all local variables in bytes)
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
    
             Global  variables  exist  at  absolute  addresses  and  may  be
          referenced directly by name from within assembler  programs.  Keep
          in mind however, that MICRO-C uses only the first 15 characters of
          a symbol's name. Also, many code generators will reduce  the  size
          of names even further, often using an algorithm  to  compress  the
          name rather than simply truncating it. For this reason,  it  is  a
          good idea to avoid using global symbol names which are longer than
          8 characters if they are to be  referenced  from  within  assembly
          language programs.

    MICRO-C                                                          Page: 34


       4.3 Compiling for ROM
    
             Assuming  the  code  generator   does   not   employ   "tricky"
          programming techniques such as self  modifying  code,  the  output
          from the compiler is entirely "clean", and may be placed  in  Read
          Only Memory (ROM).
    
             The compiler places all initialized  global  variables  in  the
          output file as part of the code image. When the program is  stored
          in ROM, those variables are also stored in ROM, and  will  not  be
          modifiable.
    
             When the program is to be placed in ROM, you may not initialize
          any variables which you intend to modify  later.  Those  variables
          must be explicitly initialized by code executed at  the  beginning
          of the program.
    
             Initialized variables which you do not intend to  modify  (such
          as tables etc.) may be initialized in the declaration, and will be
          permanently saved in the ROM as part of the static code image.
    
             The  processor  stack  pointer  must  be  set  up  before   any
          expressions are evaluated, or any function  calls  are  performed.
          One way to do this is with inline assembly statements at  the  top
          of the file.
    
             All non-initialized global variables must be  located  in  RAM.
          The compiler usually outputs all such variables at the very end of
          the compilation, just after dumping the literal pool.  The  global
          variables may be moved to RAM by  editing  the  output  file,  and
          placing an appropriate "ORG" statement at  the  beginning  of  the
          globals.
    
             You must also be sure to relocate the temporary location  which
          is defined in the startup code and runtime library  ("?temp"),  as
          well  as  any  global  variables  used  in  the  standard  library
          functions.

    MICRO-C                                                          Page: 35


    5. THE MICRO-C COMPILER
    
          The heart of the MICRO-C programming environment is the  COMPILER.
       This program reads a  file  containing  a  'C'  source  program,  and
       translates it into an equivalent assembly language program.
    
          The compiler includes its  own  limited  pre-processor,  which  is
       suitable for  compiling  programs  requiring  only  non-parameterized
       MACRO substitution, simple INCLUDE file capability, and  single-level
       CONDITIONAL processing.
    
       5.1 The MCC command
    
             When  created  using  the  'io'  routines   supplied   on   the
          distribution disk, the format of the MICRO-C Compiler command line
          is:
    
                    MCC [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCC will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  generated
          assembly language code is written. If less than two filenames  are
          specified, MCC will write to standard output.
    
          5.1.1 Command Line Options
    
                -c      - Includes the 'C' source code in the output file
                          as assembly language comments.
    
                -f      - Causes the compiler to "Fold" its literal pool.
                          (Identical strings not contained in explicit
                          variables only once in memory).
    
                -l      - Enables MCC to accept line numbers.
                          (At beginning of line, followed by ':').
    
                -q      - Instructs MCC to be quiet, and not display the
                          startup message when it is executed.

    MICRO-C                                                          Page: 36


    6. PORTING THE COMPILER
    
          There are two major goals to accomplish when porting  the  MICRO-C
       compiler to a new machine. The first is to make the compiler  run  in
       the new environment, and the second is to make it  produce  code  for
       that environment.
    
          These two goals do not always go hand in hand. For example, it may
       be desirable to implement a CROSS COMPILER which generates code for a
       different system from that on which it runs.
    
          The usual method of porting a compiler to system A when a  version
       of the compiler is already running on system B, is to first create  a
       compiler which runs on system B, producing code for  system  A.  This
       "new" compiler may then be used to create a compiler  which  runs  on
       system A.
    
          The compiler consists of a module "compile"  which  contains,  the
       main compiler, input scanner, regular expression parser,  and  symbol
       table management routines.  This  is  the  "static"  portion  of  the
       compiler which does not change in different implementations.
    
          To create a working compiler, the above module  must  be  compiled
       and linked with an "io" module and "code"  module.  The  "io"  module
       performs the necessary initialization and I/O to allow  the  compiler
       to run in a particular  environment  (goal  #1).  The  "code"  module
       generates  the  assembly  language  output  code  for  a   particular
       environment (goal #2).
    
          The compiler uses NO system library functions, and  relies  on  NO
       system services (other  than  those  used  by  the  "io"  and  "code"
       modules). This allows the compiler to  be  ported  to  virtually  any
       system.
    
          All fixed compiler  parameters  (such  as  table  sizes  etc)  are
       contained in the header file "compile.h".  When  porting  to  systems
       with very limited RAM (less than 64k), you may have to reduce some of
       these sizes in order to get it to fit.
    
       6.1 The "io" module
    
             The "io" module required  by  the  compiler  must  contain  the
          following function definitions:
    
             The function "main()" is called by the  operating  system  when
          the MICRO-C compiler is executed. It is  responsable  for  parsing
          any parmeters and command qualifiers, opening the input and output
          files,  performing  any  other  initializations  that   might   be
          required, and then  invoking  the  function  "compile()"  with  no
          arguments. The program filename should also  be  copied  into  the
          array 'file_names' found in compile.c. The "compile"  function  is
          internal to the "compile.c" module, and  will  never  return.  For
          UNIX and other systems which support I/O redirection, "stdin"  and
          "stdout" are often used for the input and output files.

    MICRO-C                                                          Page: 37


             The function "terminate(rc)" is called when  the  compiler  has
          finished all processing and wishes to terminate. The value "rc" is
          a return code: 0 = Success, program compiled without error,  -1  =
          Compile was aborted due to severe errors, n  =  Compile  finished,
          but had 'n' errors.
    
             The function "put_chr(chr, flag)"  is  passed  a  character  to
          output, as well as a flag. The flag will always be zero  when  the
          character is being sent to the console terminal, or non-zero  when
          the character is to be written to the output file.
    
             The function "put_str(*ptr, flag)" is passed  a  pointer  to  a
          zero terminated string, which is to be written to the  console  or
          output file as determined by "flag".
    
             The function "put_num(number, flag)" is passed a 16 bit number,
          which is to be written in printable form to the console or  output
          file as determined by "flag".
    
             The function "get_lin(*ptr)" is passed a pointer to a character
          array, and should read a single line from the currently open input
          file into that array. The manifest definition  "LINE_SIZE",  found
          in "compile.h" may be used to determine the  maximum  line  length
          acceptable to the compiler. Return of a non-zero  value  indicates
          the end of file condition.
    
             The function "f_open(*ptr)" is passed a pointer to a  filename.
          The new file should be opened, and if successful,  the  old  input
          file should remain open and be "stacked", so that it can be  later
          returned to, and a non-zero value returned. A zero value indicates
          to the compiler that the file could not be opened.
    
             The  function  "f_close()"  is  responsible  for  closing   the
          currently  open  input  file,  and  returning  to  the   "stacked"
          previously open one. It receives  no  parameters.  Note:  multiple
          "opens"  may  be  stacked  -  see  the  manifest   definition   of
          "INCL_DEPTH" in the "compile.h" file.
    
          6.1.1 Notes on I/O module
    
             1) It is the responsibility of the "put" routines to  translate
                the  NEWLINE  '\n'  (0x0a)  character  into  whatever   line
                termination  character(s)  are  required   by   the   target
                operating system.
    
             2) If unix "stdin"  and  "stdout"  are  not  used,  it  is  the
                responsibility  of  "main"  to  display  appropriate   error
                messages if the input or output files could not be opened.
    
                Refer to  the  sample  "io"  modules  distributed  with  the
             compiler.

    MICRO-C                                                          Page: 38


       6.2 The "code" module
    
             In order to insure that MICRO-C is portable  to  virtually  any
          environment,  the  compiler  makes  few  assumptions   about   the
          processor or system software of  the  target  system.  The  "code"
          module is relied  on  to  produce  all  machine  instructions  and
          assembler directives written to the output file.
    
             The only two real "assumptions" made about the target processor
          are:
    
          1) It is assumed that the target processor  has  an  "accumulator"
             register in which all math operations are performed,  and  that
             the  lower  8  bits  of   this   register   may   be   accessed
             independantly.
    
          2) It is  assumed  that  the  target  processor  has  one  "index"
             register which may be loaded with a  16  bit  value,  and  that
             memory references may be made indirectly through this register.
    
             If the target processor does not support the above features, it
          may be possible to write a code generator for it using some  other
          features of the processor.
    
             For example, if an "index" register  does  not  exist,  it  may
          often be implemented using two bytes of reserved memory.
    
             The code  generation  module  required  by  the  compiler  must
          contain the following function definitions:
    
             The function  "do_comment(*ptr)"  is  passed  a  pointer  to  a
          character string, which is should write to the output  file  as  a
          single line COMMENT (used by '-c' option). This function  is  also
          called with a NULL (0)  pointer  anytime  the  compiler  wants  to
          insure that the code generator is reset to begin  a  new  line  of
          output.
    
             The function "do_asm(*ptr)" is passed a pointer to a  character
          string, which it should write to the output file as a single  line
          STATEMENT (used for inline assembly language).
    
             The function "def_module()"  is  called  at  the  beginning  of
          compilation, before any other code generator functions are called.
          It is used to output any pre-amble needed by the assembler.
    
             The function "end_module()"  is  called  at  the  very  end  of
          compilation, and is the last code generator function called. It is
          used to output any post-amble needed by the assembler.

    MICRO-C                                                          Page: 39


             The function "def_static(symbol, ssize)"  is  passed  am  index
          into the compiler symbol tables for a global  variable,  which  is
          about to be initialized  as  static  storage.  The  call  to  this
          function will be immediately followed by a call  to  "init_static"
          or "end_static". The "ssize" parameter will  be  non-zero  if  the
          variable is a structure or union.
    
             The "init_static(token, value,  word)"  function  is  passed  a
          token and value, with which it should initialize a single  element
          of static storage. The "word" flag will be non-zero if  the  value
          is a 16 bit element. Only the "constant" tokens  (NUMBER,  STRING,
          LABEL) and SYMBOL need be handled by this routine. When SYMBOL  is
          used,  the  constant  ADDRESS  of  the  passed  symbol  should  be
          generated.
    
             The  "end_static()"  function  is  called  to   terminate   the
          definition of static storage.
    
             NOTE: "init_static"  should  not  rely  on  "def_static"  being
          called first,  since  it  is  also  called  immediately  following
          "def_label" to define "switch" tables (See "do_switch"). After the
          table  is  defined,  the  compiler  will  call  "end_static()"  to
          terminate the initialization and set up for the next.
    
             The function "def_global(symbol, size)" is called at the end of
          the compile, once for each non-static global  variable  which  was
          defined. The "size" paremeter indicates the  number  of  BYTES  of
          memory to be reserved for that variable.
    
             The function "def_extern(symbol)" is called at the end  of  the
          compile, once  for  each  unresolved  external  symbol  which  was
          defined. This routine should examine the type of  the  symbol  and
          output the appropriate assembler directives  to  allow  it  to  be
          referenced in another module.
    
             The "def_func(symbol, size)"  routine  is  called  to  start  a
          function definition. The "symbol" parameter is an index  into  the
          compiler symbol tables for the function entry being  defined.  The
          "size" parameter indicates how many  bytes  of  memory  should  be
          allocated  on  the  stack  for  local  variables.  When   defining
          "register" functions, care must  be  taken  that  the  entry  code
          preserves the contents of the accumulator.
    
             The "end_func()" routine is  called  to  terminate  a  function
          definition.  It  should  remove  anything  placed  on  the   stack
          (including the local variable space allocated by "def_func"),  and
          terminate the function with a "return" instruction.
    
             The "def_label(label)" function is called whenever the compiler
          wants to generate a label in the output file. Each label generated
          by the compiler is identified by a 16 bit unsigned number.  It  is
          up to the code generator to generate a unique label  suitable  for
          the target assembler.

    MICRO-C                                                          Page: 40


             The "def_literal(*ptr, size)" function is called at the end  of
          the  compile,  just  before  non-initialized  global  symbols  are
          generated. This routine is  given  a  pointer  to  the  compiler's
          "literal pool", which contains all the character strings  occuring
          during the compilation. The "size" parameter  indicates  how  many
          characters are in the pool. This pool must  be  generated  in  the
          output file as a string of byte constants.
    
             The "call(token, value,  type,  clean)"  function  is  used  to
          generate  a  machine  language  subroutine  call  to  the   entity
          indicated by the "token, value & type" parameters (See later). The
          "clean" parameter indicates how many entries were pushed onto  the
          stack as arguments, which should be removed following the function
          call.  Note:  Since  stack  entries  are   TWO   bytes   in   most
          implementations, the "clean" value must be multiplied  by  two  to
          get the actual number of bytes to be removed from the stack.
    
             The function "jump(label,  ljmp)"  is  called  to  generate  an
          unconditional jump instruction to the indicated compiler generated
          label. The "ljmp" flag will be set to zero if the jump  references
          code within the same expression from which it  is  generated,  and
          non-zero if one or more statements may occur between the jump  and
          the destination label. This allows  the  code  generator  to  take
          advantage of "short" jumps if they are available on the target.
    
             The function "jump_if(cond, label, ljmp) is called to  generate
          a conditional jump to a compiler generated label. The "cond" value
          indicates the condition: FALSE = Jump if accumulator is zero, TRUE
          = jump if accumulator is non-zero. Remaining  parameters  are  the
          same as above.
    
             The function "do_switch(label)" is  passed  the  address  of  a
          "switch" table, which contains 16  bit  entries,  and  is  of  the
          following format:
    
                        label-1, value-1, label-2, value-2, ....
                        label-n, value-n, 0, default_label
    
             This routine should search the table for the value currently in
          the accumulator, and if found, it  should  proceed  to  the  label
          associated with that value. If the value is not found  before  the
          end of the table is encountered (identified by a  label  value  of
          zero), execution should  proceed  at  the  address  identified  by
          "default_label".
    
             The "index_ptr(token, value, type)"  routine  should  load  the
          index register with the value  of  the  entity  indicated  by  the
          "token, value & type" parameters. This will always  be  a  16  bit
          wide quantity.

    MICRO-C                                                          Page: 41


             The "index_adr(token, value, type)"  routine  should  load  the
          index register with the 16 bit address of the  object  represented
          by "token, value & type". The only tokens passed to  this  routine
          are SYMBOL and ION_STACK.
    
             The routine "expand(type)" is called following  the  evaluation
          of expressions in "return" and "switch" statements, and is used to
          insure that the result is a 16 bit value.
    
             The routine "accop(oper, type)" is  called  to  perform  a  "no
          operand" operation on the accumulator. See "compile.h" for a  list
          of these operations. The "type" passed indicates the type of value
          expected as a result.
    
             The routine "accval(oper, rtype, token, value, type)" is called
          to perform a "one  operand"  operation  on  the  accumulator.  See
          "compile.h" for a list of these operations. "rtype" indicates  the
          type of value expected as a result. "token",  "value"  and  "type"
          indicate  the  location  and  type  of  operand  which  is   being
          processed.

    MICRO-C                                                          Page: 42


          6.2.1 Notes on code generation
    
                The meaning of the individual bits  in  the  16  bit  "type"
             value which is passed to many of the code generation  routines,
             is documented in the "compile.h" file.
    
                The meaning of "token"  is  documented  in  the  "compile.h"
             file. For  each  type  of  "token",  "value"  has  a  different
             meaning:
    
                Token           Meaning of "value"
                ----------------------------------------------------------
                NUMBER          The numeric value of the constant.
                STRING          The offset into the literal pool.
                LABEL           The value of the compiler generated label.
                SYMBOL          Index into global symbol tables.
                All others      Undefined.
    
                When token is a SYMBOL, the "value" passed is used to  index
             into the global symbol tables (contained within  the  "compile"
             module) to  determine  information  about  the  variable.  When
             "value" is  less  than  the  value  of  the  compiler  internal
             variable 'global_top', the symbol is GLOBAL,  otherwise  it  is
             LOCAL:
    
                s_name[value]   - Name of symbol (up to SYMBOL_SIZE chars)
                s_type[value]   - Type of symbol (bits defined in "compile.h").
                s_index[value]  - Variable index:
                        Local (auto):   Stack offset from def_func.
                        Argument:       Stack offset from last argument pushed.
                        Static:         Unique variable number for symbol.
    
                When calculating the stack offset for  ARGUMENTs,  you  must
             add the number of bytes placed on the stack when  the  function
             was called. This  includes  the  local  variables,  the  return
             address, and any other values that "def_func" might push.
    
                There are two popular ways of  providing  addressability  to
             local variables:
    
                If the processor has many registers, you can reserve one  as
             a "base" pointer, and point it at the top of the stack when the
             function  is  entered.  This  allows  local  variables  to   be
             referenced as negative offsets from that "base"  register,  and
             arguments to be referenced as positive offsets  from  it.  This
             approach also allows the stack to  be  restored  directly  from
             this base  register  when  the  function  terminates.  See  the
             section on assembly language interfacing.
    
                Another approach is to have the  code  generator  "remember"
             exactly how many bytes have been pushed onto  the  stack  since
             "def_func", and adjust the offsets it generates  based  on  the
             stack contents. This has  the  advantage  of  not  tying  up  a
             register.

    MICRO-C                                                          Page: 43


                If you intend to use the MICRO-C Source Linker (SLINK), then
             you have to insure that whatever variable you use to  reference
             the "literal pool" qualifies as a "compiler  generated"  label,
             allowing SLINK to adjust it when processing the  source  files.
             Compiler  generated  labels  normally  consist  of   a   single
             character (such as '?'), followed by a  decimal  number.  Since
             the compiler begins generating its labels with the  value  '1',
             you may safely use '0' as the literal pool variable (Ie: '?0').
    
                It is the responsibility of the code generator to keep track
             of the validity  of  the  upper  8  bits  of  the  accumulator.
             Appropriate sign extension or clearing of  high  bits  must  be
             performed as necessary to convert signed and unsigned character
             values when 16 bit results when required.
    
                To improve the effiency of conditional statements, the  code
             generator should keep track of the validity of the "zero"  flag
             in  the  processor's  condition  code  register,  and  generate
             appropriate  "test"  instructions  only  if  necessary  when  a
             conditional jump is compiled.
    
                For  processors  not  supporting   operations   with   stack
             contents, the "ON_STACK" and "ION_STACK" tokens may implemented
             by first popping the top of the  stack  into  a  register.  The
             "ISTACK_TOP" token is a special case, because  the  address  on
             the top of the stack must  not  be  lost.  This  token  may  be
             efficiently implemented, because "ISTACK_TOP" is only used  for
             read/write operations to  a  stacked  calculated  address.  For
             example:
    
                            array1[i] += array2[i];
    
                This statement calculates the address of "array1[i]" (in the
             index register). Since the "index" register is  again  used  in
             calculating the address of "array2[i]", the first "index"  will
             be placed on the stack. Once the contents  of  "array2[i]"  are
             retrieved, it  will  be  added  using  "ISTACK_TOP",  and  then
             re-stored using "ION_STACK".
    
                The "ISTACK_TOP" token may  thus  pop  the  address  into  a
             register, and set a flag indicating to the code generator  that
             the next "ION_STACK" token  is  to  go  through  that  register
             rather than the top of the stack. Note that since an arithmetic
             operation may be performed between the two references, you must
             not use a register which is  modified  in  code  generated  for
             arithmetic operations.
    
                Refer to the sample code  generators  distributed  with  the
             compiler.

    MICRO-C                                                          Page: 44


       6.3 The "compile" module
    
             The "compile" module  contains  the  main  statement  analyser,
          input  scanner,  expression  parser  and  symbol  table  managment
          routines for the MICRO-C compiler. This module is  common  to  all
          implementations, and should NOT require changes in most cases. The
          source code for this module is contained in the  "compile.c"  file
          on your distribution diskette, and may  be  examined  for  insight
          into the internal operation of the compiler.
    
             This module must be compiled and linked with your I/O and  code
          generation routines to  generate  a  complete  executable  MICRO-C
          compiler.
    
             To test your code generator,  the  file  "test.c"  is  provided
          which when compiled using the new compiler, performs a  number  of
          simple tests  to  verify  your  code  generator.  This  is  not  a
          comprehensive analysis, as  it  makes  no  assumptions  about  the
          processor, however, it provides a good indication that  your  code
          generator is on the right track.
    
             A number of fixed parameters to the  compiler  (such  as  table
          sizes etc.) are contained in the header file "compile.h". The most
          common reason for changing  these  parameters  is  to  reduce  the
          memory requirements, in order to get  MICRO-C  to  fit  into  very
          small systems.
    
             If any of the parameters in "compile.h" are to be changed,  you
          must  make  the  changes  BEFORE  compiling  any  of  the  modules
          (compile, io or codegen).
    
             The file  "tokens.h"  contains  symbolic  definitions  for  the
          tokens parsed by the  compiler,  the  text  of  which  is  in  the
          character array variable "tokens". If you make any changes to this
          token table, MAKE SURE that the contents of the "tokens"  variable
          and the "tokens.h" file agree, otherwise, you will end up  with  a
          compiler for a very strange language.
    
          6.3.1 **NOTE for 32 bit compiler users
    
                COMPILE.C has one potential portability  problem  if  it  is
             compiled on a machine where  an  'int'  is  not  16  bits.  The
             routine "skip_comment()" uses a 16 bit 'int' to hold  the  last
             two characters from the source file, in order to test  for  the
             "/*" and "*/" sequences.
    
                If an 'int' can contain more that TWO characters,  you  must
             modify this function so that only the last two  characters  are
             retained.

    MICRO-C                                                          Page: 45


       6.4 Porting without a linker
    
             It is possible to port MICRO-C using a system  which  does  not
          support a linker. To do this, you must concatinate all the  source
          files "compile.c", "code.c" and "io.c" into  one  large  file  (in
          that order), and compile them all as one program.
    
             When this is done, the ".h" include files need only be included
          once, and external definitions  of  variables  occuring  in  other
          source files should not  be  used.  The  source  programs  on  the
          distribution disk all contain conditional  compilation  statements
          (#ifndef), which only perform the necessary #include and  external
          definition statements when compiling as a single file.
    
       6.5 Optimization Techniques
    
             The MICRO-C compiler performs the following machine independant
          optimizations of the output file:
    
          1) All constant expressions are evaluated  at  compile  time,  and
             expressed as a single constant value in the output code.
    
          2) Commutative operations may be reversed  to  take  advantage  of
             partial results  already  in  the  accumulator.  This  includes
             operations which have an equivalent reverse (ie: "a>(b-1)"  may
             become "(b-1)<a").
    
          3) Redundant jumps as a result of "return" or  "break"  statements
             are suppressed.
    
          4) The sense of jumps in conditional statements are  reversed  for
             logically negated expressions, code for '!' is  only  generated
             if the value returned by that operator is actually used.
    
          5) Jumps between code generated within  a  single  expression  are
             flagged as "short".
    
             Although the MICRO-C compiler produces fairly  reasonable  code
          for the  processor  model  it  uses,  that  model  is  necessarily
          limited, in order that it might fit a  large  number  of  physical
          targets. There are  several  simple  optimizations  which  may  be
          performed to further enhance the code generated by the compiler in
          a specific implementation.

    MICRO-C                                                          Page: 46


          6.5.1 Register Usage
    
                MICRO-C assumes a single accumulator,  and  a  single  index
             register.  Additional  terms  in  complicated  expressions  are
             handled by placing temporary results on  the  processor  stack,
             and re-using those registers. All data placed on the  stack  is
             accessed on a "last in - first out" basis.
    
                If the target processor has a  full  compliment  of  general
             purpose registers, an optimization may be performed  by  simply
             selecting another general purpose register as  the  accumulator
             or index register instead of placing the value  on  the  stack.
             The code generator must  keep  track  of  the  order  in  which
             registers are selected, and which register represents the "top"
             of the stack. If the number  of  values  "pushed"  exceeds  the
             number of available registers, the "oldest" register should  be
             placed on the stack, thereby allowing it to be re-used.
    
          6.5.2 Jump Optimization
    
                Although MICRO-C identifies jumps to instructions which span
             more than one expression as "long",  often  the  addresses  are
             close enough together that short jumps may  actually  be  used.
             This optimization is particularily useful for  processors  such
             as the 8086, which does not support "long"  conditional  jumps,
             and therefore must simulate them with a short conditional  jump
             of the opposite sense around a long unconditional jump.
    
          6.5.3 Redundant Load Elimination
    
                Since  MICRO-C  evaluates  and  processes   each   statement
             individually, it  does  not  carry  partial  results  from  one
             statement to another.
    
                Consider the following statements:
    
                                 a = x;
                                 b = a + 1;
    
                MICRO-C generates the code:
    
                                 LOAD x
                                 STORE a
                                 LOAD a
                                 ADD 1
                                 STORE b
    
                An optimization may be performed  by  recognizing  that  the
             second "load" instruction is redundant, and can be  eliminated.
             Note: A more efficent (but less readable)  way  of  coding  the
             above statements which would result in the latter code  without
             optimization is:
    
                                 b = (a = x) + 1;

    MICRO-C                                                          Page: 47


          6.5.4 Peephole Optimization
    
                Consider the statement:
    
                                 a = *++ptr;
    
                MICRO-C generates the code:
    
                                 LOAD ptr
                                 INCREMENT
                                 STORE ptr
                                 MOVE ACCUMULATOR TO INDEX
                                 LOAD [INDEX]
                                 STORE a
    
                For a processor supporting  a  rich  set  of  direct  memory
             addressing modes, the above sequence can be shortened to:
    
                                 INCREMENT_MEMORY ptr
                                 LOAD [ptr]
                                 STORE a
    
                One of the most  successful  techniques  of  optimizing  the
             output code is also one of the simplest.  Known  as  "peephole"
             optimization, the method consists of keeping a  window  of  the
             last few instructions generated,  and  scanning  the  list  for
             known patterns every time a new instruction is added to it.
    
                As long as the instructions in the list at  least  partially
             match one or more  of  the  "predefined"  patterns,  additional
             instructions are collected  until  either  a  complete  pattern
             match occurs, or all known patterns are eliminated.
    
                If no matches occur, the "oldest" instruction is written  to
             the output file, and the next one  becomes  the  first  in  the
             "window".
    
                Whenever a pattern is discovered, it is replaced  by  a  new
             series of instructions which perform the same function, but  in
             a more efficent manner.
    
                The new instruction sequences  are  replaced  on  the  list,
             which may then be  again  scanned,  allowing  further  possible
             reductions to be discovered.
    
                Handling of labels in the "window" and  their  corresponding
             placement in the output file must be carefully done,  in  order
             to preserve the "logical" context of the original code.

    MICRO-C                                                          Page: 48


    7. THE MICRO-C PREPROCESSOR
    
          The MICRO-C Preprocessor is a source code filter,  which  provides
       greater capabilities than the preprocessor which is integral  to  the
       MICRO-C compiler. It has been implemented as a  stand  alone  utility
       program which processes the source code before it is compiled.
    
          Due to the higher complexity of  this  preprocessor,  it  operates
       slightly slower than the the integral MICRO-C preprocessor.  This  is
       mainly due to the fact that it reads each line from the file and then
       copies it to a new line while performing the macro substitution. This
       is necessary since each macro may contain parameters  which  must  be
       replaced "on the fly" when it is referenced.
    
          The integral MICRO-C preprocessor is very FAST,  because  it  does
       not copy the input line. When it encounters a '#define'd  symbol,  it
       simply adjusts the input scanner pointer to point to  the  definition
       of that symbol.
    
          Keeping the extended preprocessor as a stand alone utility  allows
       you  to  choose  between  greater   MACRO   capability   and   faster
       compilation. It also allows the system to continue  to  run  on  very
       small hardware platforms.
    
          The additional capabilities of the extended preprocessor are:
    
            - Parameterized MACROs.
    
            - Multiple line MACRO's.
    
            - Nested conditionals.
    
            - Ability to undefine MACRO symbols.
    
            - Library reference in include file names.

    MICRO-C                                                          Page: 49


       7.1 The MCP command
    
             The format of the MICRO-C Preprocessor command line is:
    
                    MCP [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCP will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  processed
          source code is written. If less than two filenames are  specified,
          MCP will write to standard output.
    
          7.1.1 Command Line Options
    
                MCP accepts the following command line [options]:
    
                -c      - Instructs MCP to keep comments from  the input
                          file (except for those in '#' statements which
                          are always removed). Normally, MCP will remove
                          all comments.
    
                -l      - Causes the output file to contain line numbers.
                          Each line in the output file will be  prefixed
                          with the line number of the  originating  line
                          from the input file.
    
                l=path  - Defines the directory path which will be taken
                          to reference  "library"  files when  '<>'  are
                          used around an  '#include'  file name.  Unless
                          otherwise specified, the path defaults to:
                                        '\mc'
    
                -q      - Instructs MCP to be quiet, and not display the
                          startup message when it is executed.
    
          <name>=<text> - Pre-defines a non-parameterized macro  of  the
                          specified <name> with the string value <text>.

    MICRO-C                                                          Page: 50


       7.2 Preprocesor Commands
    
             The following commands are recognized by the MCP utility,  only
          if they occur at the beginning of the source file line:
    
          7.2.1 #define <name>(parameters) <replacement text>
    
                Defines a global macro name which will be replaced with  the
             indicated <replacement text> wherever it occurs in  the  source
             file.
    
                Macro  names  may  be  any  length,  and  may  contain   the
             characters 'a'-'z', 'A'-'Z', '0'-'9' and '_'.  Names  must  not
             begin with the characters '0'-'9'.
    
                If the macro name is IMMEDIATELY followed by a list of up to
             10 parameter names contained in brackets, those parameter names
             will be substituted with parameters passed to the macro when it
             is referenced. Parameter names follow the same rules  as  macro
             names.
    
                     eg: #define min(a, b) (a < b ? a : b)
    
                If any spaces exist between the macro name and  the  opening
             '(', the macro will not be  parameterized,  and  all  following
             text (including '(' and ')') will be  entered  into  the  macro
             definition.
    
                If the very last character of a  macro  definition  line  is
             '\', MCP will continue the definition with the next  line  (The
             '\' is not included). Pre-processor statements included as part
             of a macro definition will not be processed by MCP, but will be
             passed on and handled by the integral MICRO-C preprocessor.
    
          7.2.2 #undef <symbol>
    
                Undefines the named macro symbol. further references to this
             symbol will not be replaced.
    
                NOTE: With MCP, macro definitions operate on a STACK. IE: If
             you define a macro  symbol,  and  then  re-define  it  (without
             '#undef'ing it first), subsequently '#undef'ing it  will  cause
             it to revert to its  previous  definition.  A  second  '#undef'
             would then cause it to be completely undefined.

    MICRO-C                                                          Page: 51


          7.2.3 #forget <symbol>
    
                Similar  to  '#undef',  except  that  the  symbol  and   ALL
             SUBSEQUENTLY DEFINED SYMBOLS will be undefined.
    
                Useful for releasing any local symbols (used only  within  a
             single include file).
    
                For example:
    
                        #define GLOBAL "xxx"    /* first global symbol */
                            ...                 /* more globals */
                        #define LOCAL   "xxx"   /* first local symbol */
                            ...                 /* more locals */
                        /* body of include file goes here */
                        #forget LOCAL           /* release locals */
    
          7.2.4 #ifdef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is defined as a macro.
    
          7.2.5 #ifndef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is NOT defined as a macro.
    
                NOTE: '#ifdef/#ifndef#else/#endif' may be nested.
    
          7.2.6 #else
    
                Toggles the state of the "if_flag", controlling  conditional
             processing. Only has effect in the highest level  of  suspended
             processing. IE: Nested conditionals will work properly.
    
                If the previous  '#ifdef/#ifndef'  failed,  processing  will
             begin again following the '#else'.
    
                If the previous '#ifdef/#ifndef' passed, processing will  be
             suspended until the '#endif' is encountered.
    
                NOTE: Since '#else' acts as a toggle, it may be used outside
             of any '#ifdef/#ifndef' to unconditionally  suspend  processing
             up to '#endif'. You can also use multiple '#else's in a  single
             conditional,  to  swap  back  and  forth   between   true/false
             processing without re-testing the condition.
    
          7.2.7 #endif
    
                Resets  the  "if_flag"  controlling  conditionals,   causing
             processing to resume. Only has effect in the highest  level  of
             suspended  processing.  IE:  Nested  conditionals   will   work
             properly.

    MICRO-C                                                          Page: 52


          7.2.8 #include <filename>
    
                Causes MCP to open the named file and include  its  contents
             as part of the input source.
    
                If the filename is contained within '"' characters, it  will
             be opened exactly as  specified,  and  (unless  it  contains  a
             directory path) will reference a file in the current directory.
    
                If the filename is contained within the characters  '<'  and
             '>', it will be  prefixed  with  the  library  path  (See  'l='
             option), and will therefore reference a file  in  that  library
             directory. The default  library  directory  is  assumed  to  be
             '\mc'.
    
                For example:
    
                        #include "header.h"     /* from current directory */
                        #include <stdio.h>      /* from library directory */

    MICRO-C                                                          Page: 53


       7.3 Error messages
    
             When MCP detects an error during processing of an include file,
          it displays an error message, which is preceeded by  the  filename
          and line number where the error occurs. If more than 10 errors are
          encountered, MCP will terminate.
    
             The following error messages are reported by MCP:
    
          7.3.1 Cannot open include file
    
                A '#include' statement on the  indicated  line  specified  a
             file which could not be opened for reading.
    
          7.3.2 Invalid include file name
    
                A '#include' statement on the  indicated  line  specified  a
             file  name  which  was  not  contained  within  '"'   or   '<>'
             characters.
    
          7.3.3 Invalid macro name
    
                A '#define' statement on the indicated line contains a macro
             name which does not follow the name rules.
    
          7.3.4 Invalid macro parameter
    
                A '#define' statement on the indicated line contains a macro
             parameter name which does not follow the name rules.
    
                A reference to a macro does not have a proper ')'  character
             to terminate the parameter list.
    
          7.3.5 Too many errors
    
                More  than  10  errors  has  been  encountered  and  MCP  is
             terminating.
    
          7.3.6 Too many macro definitions
    
                MCP has encountered more '#define' statements  than  it  can
             handle.
    
          7.3.7 Too many macro parameters
    
                A '#define' statement on the indicated line  specifies  more
             parameters to the macro than MCP can handle.
    
          7.3.8 Too many include files
    
                MCP has encountered more nested '#include'  statements  than
             it can handle.

    MICRO-C                                                          Page: 54


          7.3.9 Undefined macro
    
                A '#undef' or '#forget'  statement  on  the  indicated  line
             references a macro name which has not been defined.
    
          7.3.10 Unterminated comment
    
                The END OF FILE has  been  encountered  while  processing  a
             comment.
    
          7.3.11 Unterminated string
    
                A quoted string  on  the  indicated  line  has  no  end.  To
             continue a string to  the  next  line,  use  '\'  as  the  last
             character on the line. The '\' will  not  be  included  in  the
             string.

    MICRO-C                                                          Page: 55


    8. THE MICRO-C OPTIMIZER
    
          The MICRO-C optimizer is an output code filter which examines  the
       assembly code produced by the compiler, recognizing known patterns of
       inefficent code (using the "peephole" technique), and  replaces  them
       with more optimal code  which  performs  the  same  function.  It  is
       entirely table driven, allowing it to be modified for  virtually  any
       processor.
    
          Due its many table lookup operations, the  optimizer  may  perform
       quite slowly when processing a large  file.  For  this  reason,  most
       people prefer not to optimize during the debugging of a program,  and
       utilize the optimizer only when creating the final copy.
    
       8.1 The MCO command
    
             The format of the MICRO-C Optimizer command line is:
    
                    MCO [input_file] [output_file] [options]
    
             [input_file] is the name of the source file containing assembly
          statements to read. If no filenames are given, MCO will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  optimized
          assembly  code  is  written.  If  less  than  two  filenames   are
          specified, MCO will write to standard output.
    
          8.1.1 Command Line Options
    
                MCO accepts the following command line [options]:
    
                -d      - Instructs MCO to produce a 'debug' display on
                          standard output showing the  source code  which
                          it is removing and replacing in the input file.
                          NOTE: If you do not specify an  explict  output
                                file, you will get the  debug  statements
                                intermixed with  the  optimized  code  on
                                standard output.
    
                -q      - Instructs  MCO  to be quiet,  and not display
                          the startup message when it is executed.

    MICRO-C                                                          Page: 56


       8.2 Porting MCO to a new processor
    
             The MICRO-C Optimizer is completely table driven, and is fairly
          easy to port to new processors.
    
             The peephole optimization table  is  called  'peep_table',  and
          consists of two  sequential  character  string  entries  for  each
          optimization, and is terminated by single NULL pointer.
    
             The first is the "take" entry, and  represents  an  instruction
          sequence which (if found) is to be removed from the  output  file.
          The second  is  the  "give"  entry,  and  defines  a  sequence  of
          instructions to be placed in the output file at that  point.  NOTE
          that due to the way the optimizer removes and replaces instruction
          in the circular "peephole" buffer, the instructions in the  "give"
          entry ARE CODED IN REVERSE ORDER.
    
             Characters in the "take" entry with the high  bit  set  ('\200'
          and higher) are special characters which  represent  any  variable
          string which may occur in the instruction sequence,  and  will  be
          replaced with the same string wherever that  character  occurs  in
          the "give" entry. If  the  same  special  character  (eg:  '\200')
          occurs more than once  in  the  "take"  entry,  the  corresponding
          strings must be exactly the same or else the entire sequence  will
          not be matched.
    
             There may be up to 8 different  such  variable  strings  within
          each entry, the lower three bits  ('\201'-\'207')  indicate  which
          variable is referenced.
    
             The 4'th bit ('\21x') when used in a  "take"  entry,  allows  a
          match only if the variable string contains only the numeric digits
          ('0'-'9'). If any other character occurs, the instruction sequence
          will not be matched. This bit has no effect when used in a  "give"
          entry.
    
             The 5'th bit ('\22x') causes  the  variable  string  to  access
          through the "complement" table (see later). When used in a  "take"
          entry, this bit allows a match only if the variable string  occurs
          in  that  table.  When  used  in  a  "give"  entry,   causes   the
          complementary string to be output from the table.
    
             The processor will stop scanning  a  variable  string  when  it
          encounters the character which  immediately  follows  the  special
          character in the "take" entry, or at the end of the input line.

    MICRO-C                                                          Page: 57


             There are cases in which you may  not  want  the  optimizer  to
          further reduce code substitued for a particular  optimization.  In
          this case, simply include a single characer comment  in  the  GIVE
          entry, in such  a  position  as  to  prevent  the  optimizer  from
          recognizing that with any further TAKE entries.
    
             The optimzer also includes a "complement" table, which provides
          the ability to define and use "opposites" within an  optimization.
          The most common use for this  feature  is  in  the  processing  of
          conditional jumps, in cases  when  an  optimization  reverses  the
          logcal sense of a jump.
    
             The complement table is called  "not_table",  and  contains  an
          even number of character string entries. The table  is  terminated
          by a single NULL pointer. Each even/odd pair of  entries  in  this
          table are considered to be complementary strings.  When  a  "give"
          entry specifies that the complement of a variable string should be
          output, this table is scanned,  and  if  the  original  string  is
          found, the corresponding complementary entry is output instead. If
          the string is not found, it is output without modification.
    
             Note that you do not have to access the complementary table  in
          both the "give" and "take" optimization entries. For example,  you
          could specify a "special character" of '\221' in the "take" entry,
          indicating that you are using variable location 1,  and  that  the
          string must occur in the complement  table.  You  could  then  use
          "\201" in the "give" entry  to  output  the  original  string,  or
          "\221" to output the complement.

    MICRO-C                                                          Page: 58


    9. THE SOURCE LINKER
    
          Many small development environments have assemblers which  do  not
       directly support an object linker. This causes  a  problem  with  'C'
       development, because the library functions must be  included  in  the
       source code, with several drawbacks:
    
        1)  There is no way to automatically tell which library functions
            to include, therefore, you must do it manually.
    
        2)  'C' library functions must be  re-compiled every  time,  in
            order to avoid conflict between compiler generated labels.
    
          The MICRO-C Source Linker (SLINK) helps overcome  these  problems,
       by automatically  joining  previously  compiled  (assembly  language)
       source code from the library  to  your  programs.  Only  those  files
       containing functions which you  reference  are  joined  (Taking  into
       consideration functions called  by  the  included  library  functions
       etc...). As the files  are  joined,  compiler  generated  labels  are
       adjusted to be unique within each file.
    
       9.1 The SLINK Command
    
             The format of the SLINK command line is:
    
                   SLINK input_file... output_file [options]
    
             "input_file" is the name of  the  source  file  containing  the
          compiler output from your program.  Several  input  files  may  be
          specified, in which case they will all be processed into a  single
          output file.
    
             "output_file" is the name of  the  file  to  which  the  linked
          source code is written.

    MICRO-C                                                          Page: 59


          9.1.1 Command line options
    
                SLINK accepts the following command line [options]:
    
                ?       - Display command line help summary.
    
                i=name  - Specify name of the External Index File.
    
                -l      - Instructs SLINK to list each library used.
    
                l=path  - Identifies the directory path which will be
                          taken to reference "library" files. If not
                          specified, it defaults to: '\mc\slib'
    
                p=char  - Identifies the PREFIX character of compiler
                          generated symbols. Defaults is '?'.
    
                -q      - Inhibit display of the startup message.
    
                t=string- Prefix to prepend to temporary filenames.
                          If not specified, default is "$".
    
                -w      - Sort WORD data to beginning of allocated bulk
                          unitialized storage (See $DD: directive).
    
       9.2 Multiple Input Files
    
             SLINK accepts multiple input files on  the  command  line,  and
          processes each file to build the output file. This allows  you  to
          "link" together several previously compiled (or assembly language)
          modules into one final program.
    
             Any external references  which  are  not  resolvable  from  the
          library are assumed to be resolved by  one  of  the  input  source
          files. Since SLINK does not have knowledge of the  public  symbols
          defined  in  the  input  files,  the  absence  of  an   externally
          referenced symbol will not be detected  until  the  assembly  step
          (where it will cause an undefined symbol error).

    MICRO-C                                                          Page: 60


       9.3 The External Index File
    
             SLINK uses a special file from the library to  determine  which
          symbols are in which files. This  files  is  called  the  EXTERNAL
          INDEX FILE, and is  found  in  the  library  directory  (see  'l='
          option), under the name "EXTINDEX.LIB".
    
             This  file  contains  entries  which  cross-reference  external
          symbols to files. Each entry is as follows:
    
            1)  Any lines beginning with '<' contain the names of files
                which are to be processed and included at the BEGINNING
                of the program (Before your source file). This the best
                way to include the startup code and any runtime library
                routines which are required  at  all  times,  and  also
                provides a method of initializing any segments used.
                    eg: <6809rl.asm
    
            2)  Any lines beginning with '^' contain the names of files
                which are to be processed AFTER the program and library
                source files, but BEFORE any  uninitialized  data areas
                are output. This is the best way to set up the location
                and storage class of the uninitialized data  if it does
                not immediately follow the executable program code, and
                also providing any postamble needed by the segments.
    
            3)  Any lines beginning with '>' contain the names of files
                which are to be processed at the END  of  the  program,
                after all other information is output. This is the best
                way to define heap memory storage,  and  to provide any
                post-amble needed by the assembler.
    
            4)  Any lines beginning with '-' contain the names of files
                which are to  be  included  if  any  of  the  following
                symbols  (Up to another '<', '^', '>', '-' or '$')  are
                referenced.
                    eg: -printf.asm format.asm fgets.asm fget.asm
    
                NOTE: In most cases, the library functions will contain
                indications of any external references that they do, in
                which case SLINK will automatically include those files
                even of the names are not mentioned on the '-' line. In
                the example above, the following would suffice:
                        -printf.asm
    
            5)  The names  of  each  symbol  which  may  be  referenced
                externally must follow the '<', '^', '>' or  '-' entry.
                Symbols must occur one per line,  with  no  leading  or
                trailing spaces.
                    eg: printf
                        fprintf
                        sprintf

    MICRO-C                                                          Page: 61


            6)  A line beginning with '$' is used to define the pseudo-
                opcode used by SLINK to reserve uninitialized  data  at
                the end of the output file.  Only  one  line  beginning
                with '$' should be entered into the EXTINDEX.LIB  file.
                The remainder of this line, including all  spaces  etc.
                is entered between each symbol name,  and  the  decimal
                size (in bytes) which is written to the output file.
                    eg: '$ RMB '    <- Quotes are for clarity
    
            A complete example:
    
                    -printf.asm
                    printf
                    fprintf
                    sprintf
                    -scanf.asm
                    scanf
                    fscanf
                    sscanf
                    <PREFIX.asm
                    ^MIDDLE.ASM
                    >SUFFIX.ASM
                    $ RMB
    
            In summary, the output file is written from:
    
                1 - The '<' (prefix) files              *
                2 - The program source files            *\
                3 - Library files referenced (if any)   * > See note
                4 - Segments 1-9 from above ...         */
                5 - The '^' (middle) files
                6 - Segments 1-9 from middle files      * See note
                7 - Uninitialized data definitions      (if any)
                8 - The '>' (suffix) files
                9 - Segments 1-9 from sufix file(s)     * See note
    
            * NOTE: If these files contain multiple segments (see later),
                    all segments are grouped and written  in  seguential
                    order. IE: Seg 0 from all files is written, followed
                    by Seg 1, etc.

    MICRO-C                                                          Page: 62


       9.4 Source file information
    
          9.4.1 SLINK Directives
    
                SLINK interpretes several "directives" which may be inserted
             in the  input  source  files  to  control  the  source  linking
             process. These directives must be on a separate line, beginning
             in column 1, and must be in  uppercase.  They  are  removed  by
             SLINK during processing, and thus will not cause conflict  with
             the normal syntax used by the assembler.
    
                                   $SE:<0-9>
    
                The '$SE' directive is used  by  SLINK  to  define  multiple
             output segments. Up to 10 segments are allowed, with segment  0
             being the default which  is  selected  when  a  file  is  first
             encountered.  Other  segments  (1-9)  when  selected  via  this
             directive are written to temporary files, and re-joined at  the
             end of processing in  sequential  order.  this  allows  you  to
             separate sections of the source file (such as initialized data,
             literal pool etc.) into distinct areas of memory.
    
                              $DD:<symbol> <size>
    
                The '$DD' directive is used  to  define  uninitialized  data
             storage areas, which will be allocated by SLINK between the '^'
             (middle) and '>' (suffix) files. This allows  you  to  allocate
             unitialized data outside of the bounds of the executable image,
             and thus exclude it from being saved to disk. This  action  may
             be thought  of  as  an  additional  (11'th)  segment  which  is
             available for uninitialized data only,  and  which  avoids  the
             temporary file read/write overhead associated with use  of  the
             other segments. This directive  is  normally  placed  into  the
             source file by the "def_global" routine  in  the  MICRO-C  code
             generator.
    
                                  $EX:<symbol>
    
                The '$EX' directuve is used by SLINK to identify any symbols
             which are externally referenced. Whenever a '$EX' directive  is
             found, SLINK  searches  the  EXTINDX.LIB  file  for  the  named
             symbol, and marks the corresponding files for inclusion in  the
             program. This directive is normally placed into the source file
             by the "def_extern" routine in the MICRO-C code generator.
    
                If you  are  writing  assembly  language  programs  for  the
             library, be sure to  include  "$SE:<0-9>"  directives  for  any
             segments you wish to access, "$DD:<symbol>  <size>"  directives
             for  any  uninitialized  data  you  wish   to   allocate,   and
             "$EX:<symbol>" directives for any symbols which you  externally
             reference. If you wish to place an assembly language comment on
             the same line, make sure it is separated from the remainder  of
             the directive by at least one space or tab character.

    MICRO-C                                                          Page: 63


                Also, note that '<' (prefix) files may contain "$SE",  "$DD"
             and "$EX" directives, '^' (middle) files may contain "$SE"  and
             "$DD" but not "$EX", and '>' (suffix) files may  only  contains
             "$SE" directives. Basically, the rule is that "$EX"  cannot  be
             used after the libraries are included and "$DD" cannot be  used
             after the uninitialized data is output. Since  the  middle  and
             suffix files  are  ALWAYS  included,  simply  insure  that  all
             external references and data declarations needed by any of them
             are performed in the '<' (prefix) file.
    
          9.4.2 Compiler generated labels
    
                As it processes each source file, SLINK scans each line  for
             symbols which consist of the '?' character (See  'p='  option),
             followed by a number. If it finds such as symbol, it inserts  a
             two character sequence ranging from 'AA' to  'ZZ'  between  the
             '?', and the number. This sequence will be incremented for each
             source file processed,  and  thus  insures  that  the  compiler
             generated symbols will be unique for each file.
    
                If you  are  writing  assembly  language  programs  for  the
             library, you must be careful to  avoid  using  identical  local
             symbols in any of the library files, one way to do this  is  to
             use symbols which meet the above criteria.
    
       9.5 The SCONVERT command
    
             SCONVERT is a utility  which  assists  in  converting  existing
          assembly language  source  files  into  a  format  which  is  more
          suitable for use by the SLINK. Two main functions are performed:
    
          1) All comments are removed, and  all  spacing  is  reduced  to  a
             single space. This minimizes the size of the  file,  and  helps
             decrease linkage time.
    
          2) All symbols defined in the file which  are  not  identified  as
             "keep" symbols are converted to resemble the  MICRO-C  compiler
             generated symbols. This allows  SLINK  to  adjust  them  to  be
             unique within each source file.
    
             The format of the SCONVERT command line is:
    
    
                 SCONVERT [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  the
          original assembly language program.  If  no  filenames  is  given,
          SCONVERT will read from standard input.
    
             [output_file] is the name of the file to  which  the  converted
          source code is written. If less  that  two  filenames  are  given,
          SCONVERT will write to standard output.

    MICRO-C                                                          Page: 64


          9.5.1 Command line options
    
                SCONVERT accepts the following command line [options]:
    
                ?       - Display command line help summary.
    
                c=char  - Identifies the character used to begin a comment
                          at the trailing end of a source line. If no 'c='
                          is defined, SCONVERT will terminate processing at
                          the first blank or tab which follows the operand
                          field.
    
                C=char  - Identifies the charcter which indicates a comment
                          line in the source code. Defaults to '*'.
    
                k=name  - Identifies a symbol name to KEEP. This symbol will
                          not be converted. Multiple 'k=' are permitted.
    
                K=file  - Identifies a file containing the names of symbols
                          to KEEP, one per line. Multiple 'K=' are permitted.
    
                p=char  - Identifies the PREFIX character which is to be used
                          for the converted symbols. Defaults to '?'.
    
                -q      - Instructs SCONVERT to be quiet, and not issue its
                          startup message.
    
                SCONVERT identifies symbols in the input source file as  any
             string beginning with 'A-Z', 'a-z', '_' or '?', and  containing
             these charcters plus the digits '0-9'. If your assembler source
             files uses any other characters in its symbols, you  must  edit
             your sources and change the symbols.
    
       9.6 The SRENUM command
    
             SRENUM  is  a  small  utility  which  re-numbers  the  compiler
          generated symbols within a assembly language source file. This  is
          useful if you have made added symbols to the  file  by  hand,  and
          wish to make it "pretty" before adding it to the library etc.
    
             The format of the SRENUM command is:
    
                  SRENUM [input_file] [output_file] [options]
    
          9.6.1 Command line options
    
                SRENUM accepts the following command line [options]:
    
                ?       - Display command line help summary.
    
                p=char  - Identifies the PREFIX character which is to be used
                          to recognize compiler generated symbols.
    
                -q      - Instructs SRENUM to be quiet, and not issue its
                          startup message.

    MICRO-C                                                          Page: 65


       9.7 The SINDEX command
    
             SINDEX is a utility  which  assists  in  the  creation  of  the
          EXTINDEX.LIB file used by SLINK. When you run SINDEX, it  examines
          all of the '.ASM' files in the current  directory,  and  writes  a
          EXTINDEX.LIB file which contains a '-' type entry for  each  file,
          and  external  symbol  entries  for  any  labels  which  it  finds
          conforming to the 'C' naming conventions (Starts with 'a-z', 'A-Z'
          or '_', and contains only 'a-z', 'A-Z', '0-9' or '_').
    
             Once  you  have  run  SINDEX,  you  must  manually   edit   the
          EXTINDEX.LIB file, and remove any file or symbol entries which you
          do not wish to have available as external references, as  well  as
          insert any necessary entries for '<', '^', '>' and '$' commands.
    
          9.7.1 Command line options
    
                SINDEX accepts the following command line options:
    
                ?       - Display command line help summary.
    
                i=name  - Specify name for index file to be written.
                          Dafault is "EXTINDEX.LIB".
    
                You may also instruct SINDEX to search for  a  file  pattern
             other than '*.ASM' by passing it as a command line parameter.
    
                                 eg: SINDEX *.A
    
       9.8 The SLIB command
    
             Once you have constructed your source  library,  you  may  from
          time to time want to make minor changes to it, either  adding  new
          functions, or removing old ones ones.
    
             You could make such changes simply by editing the  EXTINDEX.LIB
          file, however you would have to be very  careful  not  to  add  or
          delete the wrong entry, and you would have to  manually  determine
          if adding or removing the file would adversly affect the remainder
          of the library. For example, you could accidently add a  duplicate
          of another symbol name, or remove a symbol which is referred to by
          another file.
    
             To simplify maintenance of source libraries, you can  make  use
          of the "Source Librarian", a utility program which  automates  the
          addition and removal of source files, and automatically reports of
          any inconsistancies occuring in the source library.
    
             To use SLIB, you must first position yourself to the  directory
          containing the source library. And then  execute  SLIB  using  the
          command options described later to indicate the action to be taken
          on the library. If you do  not  specify  any  actions,  SLIB  will
          simply examine the library and report its size and content.

    MICRO-C                                                          Page: 66


             You may use multiple command options in a single  SLIB  command
          if you wish to add and/or remove more than one file at a time.
    
             After  executing  any  command,  SLIB  will   report   on   any
          inconsistancies which it finds in the library. If any  are  found,
          and you have used a command which caused changes, SLIB will prompt
          for permission before writing the updated library file.
    
          9.8.1 Command line options
    
                The following options control the action(s)  which  will  be
             performed by SLIB on the source library index file.
    
                ?       - Display command line help summary.
    
                ?=file  - Display information about named source file.
    
                a=file  - Add specified file as standard functions.
    
                i=index - Use the specified INDEX file, if not specified,
                          the filename 'EXTINDEX.LIB' is assumed.
    
                m=file  - Add named source file as a MIDDLE file.
    
                p=file  - Add named source file as a PREFIX file.
    
                -q      - Quiet mode: SLIB will not display informational
                          messages or ask for permission to update index.
    
                r=file  - Remove the named file from the index.
    
                s=file  - Add named source file as a SUFFIX file.
    
                -w      - Write inhibit:  SLIB will not write the updated
                          library index.  This is useful if you just want
                          to see what would happen if you add or remove a
                          file.

    MICRO-C                                                          Page: 67


       9.9 Making a source library
    
             To make a complete source linkable library, follow these  basic
          steps:
    
          1) If you have assembly language library functions, run the SINDEX
             utility to create an index file with the names of  any  symbols
             defined in them. Edit this file and remove all names which  are
             LOCAL to the files. Only the global function and variable names
             should remain. NOTE: Also leave in any other symbols  or  names
             which you don't want changed by SCONVERT.
    
          2) Use SCONVERT to convert  the  assembly  language  sources  into
             library format, using the index file created above as your KEEP
             file (K=EXTINDEX.LIB). You may send the output  files  directly
             to your source library directory.
    
          3) Edit the converted assembly  language  sources  to  change  any
             declarations for uninitialized data into '$DD' directives,  and
             to add any '$SE' and '$EX' directives which may be needed.
    
          4) Compile all of your 'C' library functions to assembly language,
             using a code generator which outputs the appropriate directives
             for SLINK. Send the ASM output files  to  your  source  library
             directory.
    
          5) From within your library  directory,  run  the  SINDEX  utility
             again. This will create  an  index  file  (EXTINDEX.LIB)  which
             contains the names of all global symbols.
    
          6) Edit the index file and remove any non-public symbol names. You
             should also change the headers for the '<', '^' and '>'  files,
             and add the '$' record for reserved memory information.
    
          7) Run the SLIB utility, to check the new  library  for  duplicate
             symbols,  unresolved  external   references   and   any   other
             inconsistancies.

    MICRO-C                                                          Page: 68


    10. THE MAKE UTILITY
    
          The MAKE utility provides a method of automating the  building  of
       larger programs consisting of more that one module. The main  benefit
       of MAKE is that it keeps track of  the  files  that  each  module  is
       dependant on, and will rebuild a module if any of  those  files  have
       been modified since  the  module  was  last  built.  This  frees  the
       programmer from  the  task  of  remembering  which  files  have  been
       changed, and the commands needed to rebuild the dependant modules.
    
       10.1 MAKEfiles
    
             To use MAKE, you must first create a MAKEFILE, which is a  text
          file containing entries for each module in the program. Each entry
          consists of a DEPENDANCY list, and a series of COMMANDS.
    
          10.1.1 MAKEfile Entries
    
                A dependency list in MAKE is a line which contains the  name
             of the module, followed by a ':', followed by the names of  any
             files on which it depends. The module name MUST begin in column
             1.
    
                When MAKE is invoked, it will process each dependancy  list,
             and  will  execute  any  following  commands  (up  to   another
             dependancy list) if (1) the module does not exist,  or  (2)  if
             any of the files to the right of the ':' have a timestamp which
             is later than that of the module. For example:
    
                main.obj : main.c main.h \\mc\\stdio.h
                    \\mc\\mcc main.c main.asm
                    masm/ml main;
                    -del main.asm
    
                In the above example, the 'main.obj' would  be  rebuilt  (by
             compiling and assembling 'main.c') if either it did not already
             exist, or any of 'main.c', 'main.h' or '\mc\stdio.h' was  found
             to have a later timestamp.
    
                The '-' preceeding the 'del' command prevents it from  being
             displayed. Unless the '-q' option is enabled, MAKE will display
             any commands not preceeded by '-' as they are executed.
    
                NOTE: To enter a single '\' in the MAKEFILE,  you  must  use
             '\\', this is because like 'C',  MAKE  uses  '\'  to  "protect"
             special  characters  which  otherwise  are  used  for   special
             functions (such as '\', '$' and '#'). The first '\'  "protects"
             the second one, allowing it to pass through as source text.

    MICRO-C                                                          Page: 69


          10.1.2 Macro Substitutions
    
                Sometimes in a MAKEFILE, you have a single file or directory
             path that you use  over  and  over  again.  If  it  is  a  long
             directory path, this may  involve  a  lot  of  typing,  and  it
             becomes inconvenient to change that name (if you want to use  a
             different directory etc.) because it is repeated many times.
    
                MAKE includes a MACRO facility, which allows you  to  define
             variable names which will be replaced with a text  string  when
             used in subsequent MAKEfile lines. Names are defined by placing
             them in the MAKEfile, followed by '=',  and  the  text  string.
             Macro names being defined MUST begin in  column  one,  and  may
             consist of the characters ('a'-'z', 'A'-'Z', '0'-'9', and '_').
    
                Whenever MAKE encounters a '$' in the  file,  it  takes  the
             name immediately following, and performs the macro replacement:
    
                mcdir = \\mc
                main.obj : main.c main.h $mcdir\\stdio.h
                    $mcdir\\mcc main.c main.asm
                    masm/ml main;
                    del main.asm
    
    
                When a macro name is immediately  followed  by  alphanumeric
             text, use a single '\' to  separate  it  from  the  text.  This
             "protects"  the  first  character  of  the  text   from   being
             interpreted as part of the macro name:
    
                mcdir = \\mc\\
                main.obj : main.c main.h $mcdir\stdio.h
                    $mcdir\mcc main.c main.asm
                    masm/ml main;
                    del main.asm
    
                There  are  several  predefined  macro  symbols  which   are
             available:
    
    
                $*      = The full name of the dependant module (name.type).
                $@      = The name only of the dependant module.
                $.      = The full name of each file in the dependancy list,
                          separated from each other by a single space.
                $,      = The full name of each file in the dependancy list,
                          separated from each other by a single comma.
                $:      = The name only of each file in the dependancy list,
                          separated from each other by a single space.
                $;      = The name only of each file in the dependancy list,
                          separated from each other by a single comma.

    MICRO-C                                                          Page: 70


                File names in the dependancy list which are preceeded by '-'
             will not be included in the '$. $, $: $;' macro expansions:
    
                mcdir = \\mc
                main.obj : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mcc $. $@.ASM
                    masm/ml $@;
                    del $@.ASM
    
          10.1.3 MAKEfile Comments
    
                Whenever MAKE encounters the '#' character in the  MAKEFILE,
             it treats the remainder of the line as a comment, and does  not
             process it:
    
                # Define Directories
                mcdir = \\mc
    
                # Build the MAIN module
                main.obj : main.c -main.h -$mcdir\\stdio.h  # Dependants
                    $mcdir\\mcc $. $@.ASM                   # Compile
                    masm/ml $@;                             # Assemble
                    del $@.ASM                              # Delete tmp
    
          10.1.4 Ordering the MAKEfile
    
                MAKE processes the MAKEfile is sequential fashion, with  the
             entries near the top being processed before  the  entries  near
             the bottom. To insure that each module is built  properly,  any
             files appearing in the dependancy list for a module  which  are
             themselves dependant  on  other  files,  should  have  MAKEfile
             entries which occur BEFORE the entries for  the  modules  which
             are dependant on them:
    
                # Define Directories
                mcdir = \\mc
                # Build the MAIN module
                main.obj : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mcc $. $@.ASM
                    masm/ml $@;
                    del $@.ASM
                # Build the SUB module
                sub.obj : sub.c -sub.h
                    $mcdir\\mcc $. $@.ASM
                    masm/ml $@;
                    del $@.ASM
                # Bind the executable file
                # NOTE: If either of the above modules is rebuilt,
                #       this entry will be guarenteed to execute.
                main.exe : main.obj sub.obj
                    LINK $:;

    MICRO-C                                                          Page: 71


       10.2 Directives
    
             Like 'C', MAKE recognizes several "directives" in the MAKEfile.
          These  directives  are  only  recognized  if  they  occur  at  the
          beginning of the input line:
    
          10.2.1 @include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "@include" in the original MAKEfile.
    
          10.2.2 @ifdef <name> [name...]
    
                Processes the following lines (up to @else of  @endif)  only
             if one of the given MACRO names is defined. NOTE: <name> should
             not be preceeded by '$', otherwise its CONTENTS will be tested.
    
          10.2.3 @ifndef <name> [name...]
    
                Processes the following lines (up to @else of  @endif)  only
             if one of the given MACRO name is NOT defined.
    
          10.2.4 @ifeq <word1> <word2> [word3...]
    
                Processes the following lines (up to @else of  @endif)  only
             if the first word matches one of the remaining  words  exactly.
             This is useful for testing the value of a defined MACRO symbol.
    
          10.2.5 @ifne <word1> <word2>
    
                Processes the following lines (up to @else or  @endif)  only
             if the first word does not match any of the following words.
    
          10.2.6 @else
    
                Processes the following lines (up to  @endif)  only  if  the
             preceeding @ifdef, @ifndef, @ifeq or @ifne was false.
    
          10.2.7 @endif
    
                Terminates @ifdef, @ifndef, @ifeq and @ifne.
    
          10.2.8 @type <text>
    
                Displays the following text.
    
          10.2.9 @abort [text]
    
                Terminates MAKE with an 'Aborted!' message. Any text on  the
             remainder of the line will be appended to the message.

    MICRO-C                                                          Page: 72


       10.3 The MAKE command
    
             The format of the MAKE command line is:
    
                           MAKE [makefile] [options]
    
             [makefile] is the name of the MAKEfile to process. If  no  name
          is given, MAKE assumes the default name 'MAKEFILE'.
    
          10.3.1 Command Line Options
    
                MAKE accepts the following command line [options]:
    
                ?       - Causes MAKE to output a short summary  of  the
                          available command line options.
    
                -d      - Instructs MAKE to operate in "debug" mode, and
                          display the commands which it  would  execute,
                          without actually executing them. This provides
                          a method of quickly testing the MAKEFILE.
    
                -q      - Instructs MAKE to be quiet, and not display the
                          informational messages and commands executed as
                          it progresses.
    
        <name>=<text>   - Pre-defines a macro  of  the  specified  <name>
                          with the string value  <text>.  This  OVERRIDES
                          any definition within the MAKEfile,  which  may
                          be used to establish a "default" value.

    MICRO-C                                                          Page: 73


       10.4 The TOUCH command
    
             TOUCH is a small utility program which sets  the  timestamp  of
          one or more files to the current or  specified  time/date.  It  is
          useful as a  method  of  forcing  MAKE  to  recognize  a  file  as
          "changed", even when it has not.
    
             For example, if  you  had  decided  to  "undo"  several  recent
          changes by restoring a backup of 'main.c', the restored file  will
          probably have a timestamp which is  older  than  the  last  module
          which was built. In this case, MAKE would be unaware that the file
          has changed, and would therefore not rebuild the module.
    
             The TOUCH command could then be used to "update" the  timestamp
          of 'main.c' to the current time, causing MAKE to recognize it as a
          changed file.
    
                                  TOUCH main.c
    
             You could also use TOUCH to force rebuilding of several files:
    
                           TOUCH main.c sub1.c sub2.c
    
             Or even ALL '.C' files:
    
                                   TOUCH *.c
    
             TOUCH can also be used to set the timestamp of  a  file  to  an
          arbritrary value, this may be useful  to  PREVENT  a  change  from
          causing an update:
    
                         TOUCH main.c t=0:00 d=31/10/80
    
             NOTE: Use of the 't=' or 'd=' parameters to  TOUCH  allows  the
          possibility that a changed file  will  go  unnoticed.  CAUTION  is
          advised.
    
             The MSDOS  implementation  of  TOUCH  supports  '-h'  and  '-s'
          options, which cause it to set  the  timestamp  of  HIDDEN  and/or
          SYSTEM files. If these options are not used, TOUCH will not affect
          those types of files.




                                    MICRO-C

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1

        1.1 Compiler Portability                                            2
        1.2 Code Portability                                                2
        1.3 The compiling process                                           3

     2. THE COMMAND CO-ORDINATOR                                            4

        2.1 The CC command                                                  4
        2.2 Using multiple object modules                                   6

     3. THE MICRO-C PROGRAMMING LANGUAGE                                    7

        3.1 Constants                                                       7
        3.2 Symbols                                                         7
        3.3 Arrays & Pointers                                              10
        3.4 Functions                                                      11
        3.5 Structures & Unions                                            12
        3.6 Control Statements                                             15
        3.7 Expression Operators                                           17
        3.8 Inline Assembly Language                                       19
        3.9 Preprocessor Commands                                          20
        3.10 Error Messages                                                21
        3.11 Quirks                                                        26

     4. ADVANCED TOPICS                                                    30

        4.1 Conversion Rules                                               30
        4.2 Assembly Language Interface                                    31
        4.3 Compiling for ROM                                              34

     5. THE MICRO-C COMPILER                                               35

        5.1 The MCC command                                                35

     6. PORTING THE COMPILER                                               36

        6.1 The "io" module                                                36
        6.2 The "code" module                                              38
        6.3 The "compile" module                                           44
        6.4 Porting without a linker                                       45
        6.5 Optimization Techniques                                        45

     7. THE MICRO-C PREPROCESSOR                                           48

        7.1 The MCP command                                                49
        7.2 Preprocesor Commands                                           50


    MICRO-C                                                Table of Contents

                                                                         Page
        7.3 Error messages                                                 53

     8. THE MICRO-C OPTIMIZER                                              55

        8.1 The MCO command                                                55
        8.2 Porting MCO to a new processor                                 56

     9. THE SOURCE LINKER                                                  58

        9.1 The SLINK Command                                              58
        9.2 Multiple Input Files                                           59
        9.3 The External Index File                                        60
        9.4 Source file information                                        62
        9.5 The SCONVERT command                                           63
        9.6 The SRENUM command                                             64
        9.7 The SINDEX command                                             65
        9.8 The SLIB command                                               65
        9.9 Making a source library                                        67

     10. THE MAKE UTILITY                                                  68

        10.1 MAKEfiles                                                     68
        10.2 Directives                                                    71
        10.3 The MAKE command                                              72
        10.4 The TOUCH command                                             73