Name:             QBTips_L.Doc                         Date:  7/93

Also See:         QBTips_A through QBTips_K


Purpose:          To provide insights and source code to help BASIC
                  programmers -- beginner through advanced.

                  Load this into your word processor or editor.  Then
                  scan it for tidbits you think will be useful.  Just
                  "cut & paste" sections you like to separate files,
                  then run the code.


Source:           Below you'll find messages captured from the FidoNet
                  Quik_Bas echo.  We captured CODE and significant tips,
                  and eliminated chatter.


Format:           Varies, depending on the author, their programming
                  style, and the question or topic.

                  A form-feed (Chr$(12)) appears after most messages.
                  This allows you to print this, and have each message
                  (ie., each topic) start on a new page.


Recommendation:   None!

                  Some of what you'll see below is brilliant.  Some
                  demonstrates very poor programming techniques.  But
                  all of it can prove useful if you have a need.

                  NOTE 1:

                  We have NOT tried all the code you see here, and some
                  of it may not run as-is.  You may have to do a little
                  editing to coax it.  One reason that code may not run
                  is that messages sometimes get truncated or mangled in
                  transmission.  Another reason is that authors make
                  mistakes (or typos).  Again, we haven't tried running
                  everything; but when you do, you'll probably quickly
                  spot places that need editing.

                  NOTE 2:

                  There may be near-duplicate messages.  The original
                  author may have refined the code, or may have found
                  errors in the original.  If you see something that
                  looks interesting, before you rely on the code, scan
                  for the topic or author to see if a new set of code is
                  below you -- more recent messages appear below. And
                  note that the next message may be in a later package.

                  NOTE 3:

                  BEFORE running any code segment, scan through it and
                  LOOK FOR code fragments which could be DISASTROUS!

                  *** We often run un-tested code fragments from a  ***
                  *** RAM or floppy disk.  And BEFORE running it we ***
                  *** scan for "c:" or "d:" (or other hard drive)   ***
                  *** letters.  And we also scan for .. (see below) ***


                  For example, scan for "OUT " -- and if you find any
                  verify that the code is OUTting the correct values
                  to the correct ports.  Typos, transmission errors
                  or programmer mistakes could send the wrong values
                  to the wrong ports.  At best, nothing will happen.
                  At worst, you might fry your monitor -- or worse.

                  Also look for INTERRUPT (or INTERRUPTx).  These functions
                  are v-e-r-y useful for invoking low-level DOS or BIOS
                  functions.  But that low-level access also comes with
                  some risks!  Programmer or transmission errors, open
                  drive doors, etc., can, at best, cause your PC to hang.
                  At worst, you could corrupt the FAT of your hard disk.


=========================================================================




 From:  CHRIS LATTNER             Sent: 05-27-93 17:27
   To:  ALL                       Rcvd: 05-29-93 09:48
   Re:  BOX ROUTINES

       WARNING::::  This is set up for COLOR monitors only.
                    If you have a MONO monitor, scan for DEF SEG
                    and change its value.

       Hi all!  I have written a group of box drawing routines for
screen 0, and I'm going to put them here in a sec'.  The advantages
between these and other assemble routines are:


  1. They are written entirely in QB for better understanding.

  2. If two lines overlap eg(| and -) then it will draw the
     appropriate angle for it.  eg(Å)

  3. All I ask is that if you write a program that uses the
     routines, that I get a copy of the SOURCE CODE.
     Thanks and here they are!!


DEFINT A-Z
DECLARE SUB InitLines ()
DECLARE SUB InitDirs (A%, B%)
DECLARE FUNCTION CharL$ (CharN%)
DECLARE SUB Box (X%, Y%, X1%, Y1%, C%)
DECLARE FUNCTION ColorVal% (FG%, BG%)
DECLARE FUNCTION Value% (X%, Y%)
DECLARE SUB PrintOut (X%, Y%, A$, Colour%)
DIM SHARED Lines%(15)
DIM SHARED Up%(3), Down%(3), Left%(3), Right%(3)
DATA 179, 3
DATA 217, 5
DATA 191, 6
DATA 180, 7
DATA 192, 9
DATA 218, 10
DATA 195, 11
DATA 196, 12
DATA 193, 13
DATA 194, 14
DATA 197, 15
.
SUB Box (X, Y, X1, Y1, C)
IF X > X1 THEN SWAP X, X1
IF Y > Y1 THEN SWAP Y, Y1
IF X1 - X < 2 THEN X1 = X1 + 1
IF Y1 - Y < 2 THEN Y1 = Y1 + 1
.
A = Value(X, Y)
FOR I = 3 TO 15
  B = Lines(I)
  IF A = B THEN A = I: EXIT FOR
NEXT I
InitDirs A, 10
Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) +
(Right(1) OR Right(2))
PrintOut X, Y, CharL$(Char), C
.
A = Value(X, Y1)
FOR I = 3 TO 15
  B = Lines(I)
  IF A = B THEN A = I: EXIT FOR
NEXT I
InitDirs A, 9
Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) +
(Right(1) OR Right(2))
PrintOut X, Y1, CharL$(Char), C
.
A = Value(X1, Y)
FOR I = 3 TO 15
  B = Lines(I)
  IF A = B THEN A = I: EXIT FOR
NEXT I
InitDirs A, 6
Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) +
(Right(1) OR Right(2))
PrintOut X1, Y, CharL$(Char), C
.
A = Value(X1, Y1)
FOR I = 3 TO 15
  B = Lines(I)
  IF A = B THEN A = I: EXIT FOR
NEXT I
InitDirs A, 5
Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) +
(Right(1) OR Right(2))
.
PrintOut X1, Y1, CharL$(Char), C
.
FOR Z1 = X + 1 TO X1 - 1
  A = Value(Z1, Y)
  FOR I = 3 TO 15
    B = Lines(I)
    IF A = B THEN A = I: EXIT FOR
  NEXT I
  InitDirs A, 12
  Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) + (Right(1) OR Right(2))
  PrintOut Z1, Y, CharL$(Char), C

  A = Value(Z1, Y1)
  FOR I = 3 TO 15
    B = Lines(I)
    IF A = B THEN A = I: EXIT FOR
  NEXT I
  InitDirs A, 12
  Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2))+ (Right(1) OR Right(2))

  PrintOut Z1, Y1, CharL$(Char), C
NEXT Z1
.
FOR Z1 = Y + 1 TO Y1 - 1
  A = Value(X, Z1)
  FOR I = 3 TO 15
    B = Lines(I)
    IF A = B THEN A = I: EXIT FOR
  NEXT I
  InitDirs A, 3
  Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) + (Right(1) OR Right(2))
  PrintOut X, Z1, CharL$(Char), C

  A = Value(X1, Z1)
  FOR I = 3 TO 15
    B = Lines(I)
    IF A = B THEN A = I: EXIT FOR
  NEXT I
  InitDirs A, 3
  Char = (Up(1) OR Up(2)) + (Down(1) OR Down(2)) + (Left(1) OR Left(2)) + (Right(1) OR Right(2))
  PrintOut X1, Z1, CharL$(Char), C
NEXT Z1
END SUB
.
FUNCTION CharL$ (CharN%)
   CharL$ = CHR$(Lines(CharN%))
END FUNCTION
.
FUNCTION ColorVal (FG, BG)
   ColorVal = BG * 16 + FG
END FUNCTION
.
SUB InitDirs (A, B)
Up(1) = A AND 1
Up(2) = B AND 1
Down(1) = A AND 2
Down(2) = B AND 2
Left(1) = A AND 4
Left(2) = B AND 4
Right(1) = A AND 8
Right(2) = B AND 8
END SUB
.
'***************************************************
'*                                                 *
'*  Call this function to initialize all the data  *
'*        nessasary for the box function           *
'*                                                 *
'*  Call by:  InitLines                            *
'*                                                 *
'***************************************************
SUB InitLines
  FOR I = 1 TO 11
    READ Num, Attrib
    Lines(Attrib) = Num
  NEXT I
END SUB
.
SUB PrintOut (X, Y, A$, Colour)
DEF SEG = &HB800
  FOR Z = 1 TO LEN(A$)
    Y& = Y
    Address& = ((Y& - 1) * 160) + (X + Z - 1) * 2 - 2
    POKE Address&, ASC(MID$(A$, Z, 1))
    POKE Address& + 1, Colour
  NEXT Z
DEF SEG
END SUB
.
FUNCTION Value (X, Y)
DEF SEG = &HB800
  Y& = Y
  Address& = ((((Y& - 1) * 80) + (X - 1))) * 2
  Value = PEEK(Address&)
DEF SEG
END FUNCTION

'



Msg #:  4911                      QUIKBAS Subboard
 From:  JIM LITTLE                Sent: 05-26-93 01:32
   To:  JOHN JANES                Rcvd: -NO-
   Re:  EQUIPMENT LIST

 >     What I want most of all is the Current video mode.  How would
 >     I mask out the AH value and get the video mode.?  Would I sim-
 >     ply divide the value of AX by decimal 240(hex F0) and then
 >     match this new value to the list of video modes from Interrupt
 >     10,00h.??  Is there another way of doing it.??  Also, could

To get AH and AL from AX, do some division:

AH = AX \ 256      'note: integer division
AL = AX MOD 256

 >     someone give me a break down of each of the registers.??  Up
 >     to this point, I have been playing a guessing game and would
 >     like to know for *sure* which ones are which.  AX I know is
 >     AH and AL, but what do the others break down into.??  One last

There are fourteen registers on the 8088/86 chip:

AX  :  accumulator              |  All of these are pretty
BX  :  base pointer [arrays]    \  much general use.  The
CX  :  counter                  /  uses I listed are their
DX  :  divisor / multiplicand   |  most common.

BP  :  base pointer [stack]
SI  :  source index       }  For copying data.  Used with
DI  :  destination index  }  DS and ES.

CS  :  code segment
DS  :  data segment
ES  :  extra segment
SS  :  stack segment

CP  :  code pointer
SP  :  stack pointer
flags  :  what it says.

The general purpose registers, AX-DX, are broken into two byte-sized
registers each.  (AH & AL, BH & BL, etc.)  More advanced chips (386,
486...) have additional registers: EAX contains the AX register and who
knows what else; I don't have any info on chips above the 8088/86.

BP, SI, and DI are theoretically general-purpose: They can store any
16-bit number.  In practice, this is only true if you're writing a
stand-alone assembly program.  Many compilers DEMAND that BP, at least,
is left alone.  These registers are not split into byte-sized
registers.

CS, DS, ES, and SS all point to segments (64K chunks of info) in which
the code, data, stack or 'extra' are stored. Once again, in a
stand-alone program, it is theoretically possible to monkey with all of
these but CS; in actuality, you're playing with fire.

The last ones, CP and SP, point to the current (or is it next?  I'll
have to look it up) instruction and the current/next item on the stack,
respectively.  These can be changed only by specialized instructions
such as JMP and PUSH & POP.

The flags register is bit-mapped; it contains the following
information:  (left to right; bit fifteen is most-significant)

bit 15: -reserved            bit 7: SF (sign)
    14: -reserved                6: ZF (zero)
    13: -reserved                5: -reserved
    12: -reserved                4: AF (auxiliary carry)
    11: OF (overflow)            3: -reserved
    10: DF (direction)           2: PF (parity)
     9: IF (interrupt enable)    1: -reserved
     8: TP (trap flag)           0: CF (carry)

Some of those 'reserved' locations may have been filled in on later
chips.  To check if one of those flags has been set,
just do this:

bit% = 'bit you're checking
IF (register.flags AND 2^bit%) THEN ItsSet ELSE ItsNot

Well, I'm afraid I've rambled on a little longer than I meant to. 
Hopefully, you'll find something useful in the morass.. :)

'



Msg #:  4943                      QUIKBAS Subboard
 From:  DOUGLAS LUSHER            Sent: 05-27-93 12:32
   To:  WAYNE VENABLES            Rcvd: -NO-
   Re:  SORT...

WV>  Im looking for a VERY fast Integer/String sort routine for my
WV>mailreader I have QuickSort but i need one which is NOT recursive!!

Here's code for a fast version of quicksort that is iterative
rather than recursive.

DEFINT A-Z
SUB QuickSort (Array%(), Lower%, Upper%)
'QuickSort, iterative rather than recursive
'based on an idea by Cornel Huth
REDIM Lo%(128)
REDIM Hi%(128)
SP% = 0
Lo%(SP%) = Lower%
Hi%(SP%) = Upper%
SP% = SP% + 1
DO
  SP% = SP% - 1
  Lo% = Lo%(SP%)
  Hi% = Hi%(SP%)
  DO
    L% = Lo%
    H% = Hi%
    M% = Array%((Lo% + Hi%) \ 2)
    DO
      DO WHILE Array%(L%) < M%: L% = L% + 1: LOOP
      DO WHILE Array%(H%) > M%: H% = H% - 1: LOOP
      IF L% <= H% THEN
        SWAP Array(L%), Array(H%)
        L% = L% + 1
        H% = H% - 1
      END IF
    LOOP WHILE L% <= H%
    IF H% - Lo% < Hi% - L% THEN
      IF L% < Hi% THEN
        Lo%(SP%) = L%
        Hi%(SP%) = Hi%
        SP% = SP% + 1
      END IF
      Hi% = H%
    ELSE
      IF Lo% < H% THEN
        Lo%(SP%) = Lo%
        Hi%(SP%) = H%
        SP% = SP% + 1
      END IF
      Lo% = L%
    END IF
  LOOP WHILE Lo% < Hi%
LOOP WHILE SP%
END SUB
'



Msg #:  4966                      QUIKBAS Subboard
 From:  FRANCOIS ROY              Sent: 05-28-93 08:21
   To:  YATISH PATEL              Rcvd: -NO-
   Re:  (R)SCREEN 9

 YP> how would I make JUST the status bar magenta?

I put this together from a short article in PC-Mag: by using the
ColorPrint subroutine, I can display text against various coloured
backgrounds in screen modes 9 and 12.  It does NOT work in screen mode
1.  In the CALL below, the CSRLIN and POS(0) are the location at which
you want to print, and the 14 and 5 are the foreground and background
colours.  NOTE: I have this coded for PDS 7.1; in QB4.5, replace SSEG by
VARSEG.

CALL ColorPrint(" Status Bar ", CSRLIN, POS(0), 14, 5)

SUB ColorPrint (TEXT$, ROW%, COL%, FC%, BC%) STATIC
REM Prints TEXT$ in EGA or VGA graphics mode with both Foreground and
' Background colours specified.  Doesn't work in graphics CGA modes.
' Achieves result by XORing text with a solid string of CHR$(219).
  DIM INReg AS REGTypeX, OUTReg AS REGTypeX
  C$ = STRING$(LEN(TEXT$), 219)       ' String of solid chars for backgrnd
  INReg.AX = &H1300             ' Video service 13h, subfunction 0
  INReg.BX = BC%                ' Background colour
  INReg.CX = LEN(TEXT$)         ' String length
  INReg.DX = 256 * (ROW% - 1) + (COL% - 1)      ' Text pos. in "origin 0"
  INReg.ES = SSEG(C$)           ' String's segment
  INReg.BP = SADD(C$)           ' String's address
  CALL InterruptX(&H10, INReg, OUTReg)     ' Output the background
  INReg.BX = (FC% XOR BC%) + &H80   ' BL=ForeColor; BH=&H80 uses XOR to draw
  INReg.ES = SSEG(TEXT$)
  INReg.BP = SADD(TEXT$)
  CALL InterruptX(&H10, INReg, OUTReg) ' Output the text, XORing w/backgrnd
END SUB
'



Msg #:  4977                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 05-27-93 17:14
   To:  ALL                       Rcvd: -NO-
   Re:  FPRINT REPOST 1/2

Hi, All!

Since there were several people (?) who didn't get the complete, I have
decided to repost it.  I should take up only 3 messages.  Below is the
demo basic file:

Victor

--------------------- cut here
DEFINT A-Z

DECLARE SUB FPrint (S$, BYVAL Attr%, BYVAL Row%, BYVAL Col%)
'   i.e.  -- FPrint "Hello, world!", 15, 1, 1

CLS

A$ = "this is a test -- 80 characters long... "
A$ = A$ + A$

PRINT "Please be patient.  Testing performance."

T! = TIMER
FOR X = 1 TO 10000
    FPrint A$, X AND 15, 3, 1   'we can afford luxury here -- COLOR!
NEXT
T! = TIMER - T!

T2! = TIMER
FOR X = 1 TO 10000
    LOCATE 4, 1
    'COLOR X AND 15
    ' better not use COLOR here.... it adds a lot of time <G>
    PRINT A$;
NEXT
T2! = TIMER - T2!

COLOR 7
CLS
PRINT "Test results for printing 78 characters:"
PRINT
PRINT CHR$(1); "   FPrint:"; T!; "seconds"
PRINT "QB's PRINT:"; T2!; "seconds"
PRINT
PRINT "Still testing..."

A$ = "z"
T! = TIMER
FOR X = 1 TO 32766
    FPrint A$, X AND 15, 20, 1   'we can afford luxury here -- COLOR!
NEXT
T! = TIMER - T!

T2! = TIMER
FOR X = 1 TO 32766
    LOCATE 20, 1
    'COLOR X AND 15    ' better not use COLOR.... it adds a lot of time
    PRINT A$;
NEXT
T2! = TIMER - T2!

LOCATE 6, 1
PRINT "Test results for printing one character:"
PRINT
PRINT "    FPrint:"; T!; "seconds"
PRINT "QB's PRINT:"; T2!; "seconds"
PRINT
PRINT "Which is faster?"

-------------- cut there

>>> The next message is the object file and the assembly source code.
   Re:  FPRINT REPOST 2/2

---- snip here
To execute this script, save it to a file and type DEBUG <filename
where "filename" is the name of this script file.
E165"FPRINT.LZH" 0
E200"XgP9gVKBhkA...kI/...jHebO.G.8M2IGZYHItmH0d2.Nq2...kdONbcoAzbi"
E23D"LhhfW31qM2AkkaNG.GpI2Im9Ot2MV0XpV3pMMZwXY.46cGAq26gMV/ocON35O"
E27A"o0GgO2/d6sPfaVmb.cG5..LHo5yQOZOcqt61s/B3jImZ7IKsQ68t2SX1kHs1U"
E2B7"/o6WE/EActhNZOtA9yN/uv7AqvfVrxRyyp8xS/OnaWebGWQfS4N0zLQ7Naze6"
E2F4"L9fS8WXbLTwJ2jhBWeVy4Vop9RzUeL8mzxHch9RLyzxudjBKOh9e7alc5iHpX"
E331"67cn.GBJRmsk2rWU0."
E100 B8 0 3C BA 65 1 33 C9 CD "!rC" BE 0 2 50 BD F2 0 55 BF 88 90
E117 "W3" DB B1 FA 8A F0 80 C1 6 32 E4 AC "<9v" 8 "<Zv" 2 2C 6 2C
E12F 7 2C 2E E3 E8 D3 E0 A C6 AA 2 D8 92 "IIMu" E0 80 FB 5C 75 9 5A
E147 59 5B B4 40 CD 21 73 7 B4 9 BA 58 1 CD 21 CD 20 7 "Error!$"
G
Q


'


Msg #:  5043                      QUIKBAS Subboard
 From:  MIKE HEBERT               Sent: 05-28-93 16:42
   To:  CALVIN FRENCH             Rcvd: -NO-
   Re:  PALETTE CHANGE USING OUT

' Here's the new and improved fade rountine . . .

' You may notice that the screen 'blinks' when it checks
' the current palette when there are bright colours on the
' screen.  I'm going to leave another message to Rich Geldreich
' and see if there is a way to read the DAC registers without theinterrupt.
' Anyways, tell me if you can optimize this.  On my system, it
' goes about 6 times faster than in the QB environment.

DEFINT A-Z
SUB FadeToBlack (SColor, EColor, FadeDelay!)
DIM xreg as RegTypeX

DIM Value(SColor TO (EColor * 1.5))
xreg.ax = &H1017: xreg.bx = SColor
xreg.cx = (EColor) - SColor
xreg.dx = VARPTR(Value(SColor))
xreg.es = VARSEG(Value(SColor))
CALL INTERRUPTX(&H10, xreg, xreg)

DEF SEG = VARSEG(Value(SColor))
offset = VARPTR(Value(SColor))

FOR X = 1 TO 63 STEP 2
   NextFadeDelay! = TIMER + FadeDelay!
   OUT &H3C8, SColor
   FOR Y = SColor + offset TO (EColor * 3) + offset
      Z = PEEK(Y)
      IF Z - X >= 0 THEN
         WAIT &H3DA, 1
         OUT &H3C9, Z - X
      ELSE
         WAIT &H3DA, 1
         OUT &H3C9, 0
      END IF
   NEXT Y
   DO
   IF NextFadeDelay! <= TIMER THEN EXIT DO
   LOOP
NEXT X
DEF SEG

OUT &H3C8, SColor
FOR X = SColor TO EColor * 3
   OUT &H3C9, 0
NEXT X
END SUB
'



Msg #:  5050                      QUIKBAS Subboard
 From:  LUIS ESPINOZA             Sent: 05-28-93 17:42
   To:  ALL                       Rcvd: -NO-
   Re:  SORTS SORTS SORTS AND 6 M

On (26 May 93) Victor Yiu wrote to Calvin French...

 VY> Calvin, I believe you have reinvented the exchange sort.
 VY> 
 VY> Victor

        On this business of sort algorithm's, It made me think of a program
        that was out on the Apple ][ systems, way back when, called
        Visi-Sort Plus, which let you actuallly see how a sort program
        really works. Intrigued by it, I decided to make one for the IBM
        (VGA monitors). The only sort I could not fit in was RapidSort,
        other from That their are 9 different sorts you can view.

                                        Luis Espinoza

'________O_/________________________| SNIP |______________________\_O_______
'        O \                        | HERE |                      / O
'This file created by PostIt! v6.0.
'>>> Start of page 1.

DECLARE SUB BubbleSort (Item%(), Count%)
DECLARE SUB ShakerSort (Item%(), Count%)
DECLARE SUB ShellSort (Item%(), Count%)
DECLARE SUB Fastsorti (Item%(), Lower%, Upper%)
DECLARE SUB QuickSort (Item%(), Lower%, Upper%)
DECLARE SUB ShellSort2 (Item%(), Count%)
DECLARE SUB SelectSort (Item%(), Count%)
DECLARE SUB InsertSort (Item%(), Count%)
DECLARE SUB IntRapidSort (IntArray%(), LowestElement%,_
 HighestElement%, LowestVal%, HighestVal%)
DEFINT A-Z
DECLARE SUB CreateArray (Item%())
DECLARE SUB ShuffleArray (Item%())
DECLARE SUB PlotIt (A%, b%, A%())

'DIM SHARED MaxArray AS LONG
CONST MaxArray = 200
REDIM Item(MaxArray)
CLS
'CONST NoPlot = 1               'Remove Comment for speed

TYPE stacktype 'for QuickSort2
  low AS INTEGER
  hi AS INTEGER
END TYPE

SCREEN 12

FOR Ds = 1 TO 9
  SELECT CASE Ds
    CASE 1
      A$ = "Bubble Sort"
    CASE 2
      A$ = "Shaker Sort"
    CASE 3
      A$ = "Selection Sort"
    CASE 4
      A$ = "Insert Sort"
    CASE 5
      A$ = "Shell Sort"
    CASE 6
      A$ = "Shell Sort2"
    CASE 7
      A$ = "Quick Sort"
    CASE 8
      A$ = "Fast Sort"
    CASE 9
      A$ = "Rapid Sort"
  END SELECT

  LINE (0, 0)-(450, 480), 0, BF

  LOCATE 1 + (2 * (Ds - 1)), 60
  PRINT A$

  CreateArray Item()
  'ShuffleArray Item()

  FOR i = 1 TO MaxArray
    PSET (i, Item(i)), 14
  NEXT


  LOCATE 22, 60
  PRINT "Sorting........."

  b! = TIMER
  SELECT CASE Ds
    CASE 1
      BubbleSort Item(), MaxArray
    CASE 2
      ShakerSort Item(), MaxArray
    CASE 3
      SelectSort Item(), MaxArray
    CASE 4
      InsertSort Item(), MaxArray
    CASE 5
      ShellSort Item(), MaxArray
    CASE 6
      ShellSort2 Item(), MaxArray
    CASE 7
      QuickSort Item(), 1, MaxArray
    CASE 8
      Fastsorti Item(), 1, MaxArray
    CASE 9
      IntRapidSort Item(), 1, MaxArray, 1, MaxArray
  END SELECT
  C! = TIMER
  FOR i = 1 TO MaxArray
    PSET (i, Item(i)), 14
  NEXT
  SLEEP 1
  FOR i = 1 TO MaxArray
    PSET (i, Item(i)), 14
  NEXT
  LOCATE 22, 60
  PRINT "                   "
  LOCATE 23, 40
  IF C! < b! THEN C! = C! + b!
  LOCATE 2 + (2 * (Ds - 1)), 60
  PRINT USING "  Elaps: ##.#######"; (C! - b!)
NEXT

END

SUB BubbleSort (Item(), Count)
  n = Count
  k = n - 1
  FOR i = 1 TO k
    l = n - i
    FOR J = 1 TO l
       IF Item(J) > Item(J + 1) THEN
   SWAP Item(J), Item(J + 1)
   PlotIt J, J + 1, Item()
       END IF
    NEXT
  NEXT
END SUB

SUB CreateArray (Item())
  LOCATE 22, 60
  PRINT "Creating Array"
  FOR i = 1 TO MaxArray
    Item(MaxArray-i+1) = i
  NEXT
END SUB

SUB Fastsorti (InArray%(), Lower%, Upper%)

  ' This routine was writen by Ryan Wellman.
  ' Copyright 1992, Ryan Wellman, all rights reserved.
  ' Released as Freeware October 22, 1992.
  ' You may freely use, copy & modify this code as you see
  ' fit. Under the condition that I am given credit for
  ' the original sort routine, and partial credit for modified
  ' versions of the routine.

  ' Thanks to Richard Vannoy who gave me the idea to compare
  ' entries further than 1 entry away.

  Increment = (Upper + Lower)
  l2 = Lower - 1

  DO
    Increment = Increment \ 2
    i2 = Increment + l2
    FOR Index = Lower TO Upper - Increment
      IF InArray(Index) > InArray(Index + Increment) THEN
  SWAP InArray(Index), InArray(Index + Increment)
  PlotIt Index, Index + Increment, InArray()
  IF Index > i2 THEN
    cutpoint = Index
    stopnow = 0
    DO
      Index = Index - Increment
      IF SGN(Index + Increment) = 1 AND SGN(Index) = 1 THEN
        IF InArray(Index) > InArray(Index + Increment) THEN
          SWAP InArray(Index), InArray(Index + Increment)
          PlotIt Index, Index + Increment, InArray()
        ELSE
          stopnow = -1
          Index = cutpoint
        END IF
      ELSE
        stopnow = -1
        Index = cutpoint
      END IF
    LOOP UNTIL stopnow
  END IF
      END IF
    NEXT Index
  LOOP UNTIL Increment <= 1
END SUB

SUB InsertSort (Item(), Count)
  FOR A = 2 TO Count
    t = Item(A)
    b = A - 1
    WHILE b >= 1 AND (t < Item(b))
      Item(b + 1) = Item(b)
      PlotIt b + 1, b, Item()
      b = b - 1
    WEND
    Item(b + 1) = t
    PlotIt b + 1, t, Item()
  NEXT
END SUB

SUB IntRapidSort (IntArray(), LowestElement, HighestElement,_
 LowestVal, HighestVal)

REDIM SortArray(LowestVal TO HighestVal)


  FOR n = LowestElement TO HighestElement
     Value = IntArray(n)
     SortArray(Value) = SortArray(Value) + 1
  NEXT n

  FOR arr = LowestVal TO HighestVal
     rep = SortArray(arr)
     FOR n = 1 TO rep
    ptr = ptr + 1
    IntArray(ptr) = arr
     NEXT n
  NEXT arr

  ERASE SortArray

END SUB

SUB PlotIt (A, b, A())
  IF NoPlot THEN EXIT SUB
  LINE (A, 0)-(A, 480), 0
  PSET (A, A(A)), 8
  LINE (b, 0)-(b, 480), 0
  PSET (b, A(b)), 8
END SUB

SUB QuickSort (SortArray(), Lower%, Upper%)
  'QuickSort iterative (rather than recursive) by Cornel Huth
  DIM lstack(1 TO 128) AS stacktype   'our stack
  DIM sp AS INTEGER                   'out stack pointer
  sp = 1
  'maxsp = sp
  lstack(sp).low = Lower%
  lstack(sp).hi = Upper%
  sp = sp + 1
  DO
    sp = sp - 1
    low = lstack(sp).low
    hi = lstack(sp).hi
    DO
      i = low
      J = hi
      mid = (low + hi) \ 2
      compare = SortArray(mid)
      DO
  DO WHILE SortArray(i) < compare
    i = i + 1
  LOOP
  DO WHILE SortArray(J) > compare
    J = J - 1
  LOOP
  IF i <= J THEN
    SWAP SortArray(i), SortArray(J)
    PlotIt i, J, SortArray()
    i = i + 1
    J = J - 1
  END IF
      LOOP WHILE i <= J
      IF J - low < hi - i THEN
  IF i < hi THEN
    lstack(sp).low = i
    lstack(sp).hi = hi
    sp = sp + 1
  END IF
  hi = J
      ELSE
  IF low < J THEN
    lstack(sp).low = low
    lstack(sp).hi = J
    sp = sp + 1
  END IF
  low = i
      END IF
    LOOP WHILE low < hi
    'IF sp > maxsp THEN maxsp = sp
  LOOP WHILE sp <> 1
  'PRINT "MAX SP"; maxsp
END SUB

SUB SelectSort (Item(), Count)
  FOR A = 1 TO Count - 1
    C = A
    t = Item(A)
    FOR b = A + 1 TO Count
      IF Item(b) < t THEN
  C = b
  t = Item(b)
      END IF
    NEXT
    Item(C) = Item(A)
    Item(A) = t
    PlotIt C, A, Item()
  NEXT
END SUB

SUB ShakerSort (Item(), Count)
  C = 1
  b = Count
  d = b - 1
  DO
    FOR A = d TO C STEP -1
      IF Item(A) > Item(A + 1) THEN
  SWAP Item(A), Item(A + 1)
  PlotIt A, A + 1, Item()
  b = A
      END IF
    NEXT
    C = b + 1
    FOR A = C TO d
      IF Item(A) > Item(A + 1) THEN
  SWAP Item(A), Item(A + 1)
  PlotIt A, A + 1, Item()
  b = A
      END IF
    NEXT
    d = b
  LOOP WHILE C < d
END SUB

SUB ShellSort (Item(), Count)
  M = Count
  DO WHILE INT(M / 2)
    M = INT(M / 2)
    FOR X = 1 TO Count - M
      h = X
      DO
  v = h + M
  IF Item(h) < Item(v) THEN EXIT DO
  SWAP Item(h), Item(v)
  PlotIt h, v, Item()
  h = h - M
      LOOP WHILE h >= 1
    NEXT
  LOOP
END SUB

SUB ShellSort2 (Item(), Count)
  DIM A(5)
  A$ = "95321"
  FOR i = 1 TO 5
    A(i) = ASC(MID$(A$, i, 1)) - ASC("0")
  NEXT
  FOR w = 1 TO 5
   k = A(w)
   FOR i = k TO Count
     X = Item(i)
     J = i - k
     DO WHILE X < Item(ABS(J)) AND J > 0 AND J < Count
       Item(J + k) = Item(J)
       PlotIt J + k, J, Item()
       J = J - k
     LOOP
     Item(J + k) = X
     PlotIt J + k, X, Item()
   NEXT
  NEXT
END SUB

SUB ShuffleArray (Item() AS INTEGER)
  LOCATE 22, 60
  PRINT "Shuffling Array";
  FOR i = 1 TO MaxArray
    SWAP Item(INT(RND * MaxArray) + 1), Item(INT(RND * MaxArray)_
 + 1)
  NEXT
END SUB

'



Msg #:  5623                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-01-93 22:54
   To:  ALL                       Rcvd: 06-04-93 14:13
   Re:  POSTIT! 6.1 --> 1/11

Hi, All!

    I'm proud to present the new version of PostIt!  I've tried to make
everything as painless as possible.  From now on, you can just run
everything through PostIt!, to encode and to decode.  Messages and
binary. Enjoy!

    By the way, the source code is only 22K, compared to 36K previously!

Victor
'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O
'This file created by PostIt! v6.1.
'>>> Start of page 1.

'ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
'º   PostIt! 6.1   THE Binary <-> BASIC Script Creator   º
'ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
'º      Rich Geldreich, Jim Giordano, Mark H Butler,     º
'º   Quinn Tyler Jackson, Scott Wunsch, and Victor Yiu.  º
'ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
'
'Purpose:
' To enable the posting of compressed listings on a text only net.
' This program takes a binary input file and converts it to a series
' of small, postable files which other people can capture and run to
' get the original binary file.  Do not post text files in binary
' PostIt! form, though.
'
' New 6.1 features:
'   o  Automatic decoding/filtering of text-scripts
'   o  Automatic extraction of binary scripts
'   o  Decreased source-code size
'
' New huge script capability to be added in a future version

DEFINT A-Z

CONST True = -1, False = NOT True
CONST LineLength = 65    ' please don't change this for safety

DIM SHARED Shift(6), Proplr$, BytesOut, TotalLinesOut, LinesOut
DIM SHARED PageLength, CurrentPage, FileLength, TabStops
DIM SHARED SourceFile$, DestFile$, RealSource$, aLength
DIM SHARED Row, Col, CheckSum, CurrentByte, CurrentBit, Char
DIM SHARED Work$, ComprChar$, Qt$, Prefix$, DefaultFile$

Good$ = "abcdefghijklmnopqrstuvwxyz"
Good$ = Good$ + UCASE$(Good$) + "0123456789#$"

Initialize
Func = GetInformation

SELECT CASE Func
    CASE 1
        ExtractFile
    CASE 2
        MrFilter
    CASE 3
        PrepareFile     ' open file, print header, etc.
        JustDoIt        ' do the binary stuff
        PrintDecoder    ' print decoder, close file

        LOCATE Row, Col
        PRINT "          "
        PRINT
        PRINT TotalLinesOut; "lines in"; CurrentPage;
        PRINT "file(s) written."
    CASE 4
        MsgSplit SourceFile$, RealSource$, DestFile$, PageLength, LinesOut
END SELECT

END

ErrorRead:
    PRINT "Error reading script."
    END

FUNCTION Analyze (Filename$)
' 1=PostIt! binary
' 2=PostIt! text
' 3=regular binary
' 4=regular text

A = 4096
IF LOF(1) < A THEN A = LOF(1)
A$ = INPUT$(A, 1)
A = INSTR(A$, "C" + "LS:?STRING$(50,178):DEFINT A-Z 'Created by PostIt! 6.")
IF A THEN
    CheckSum = A   ' use it to pass the start to decoder
    Analyze = 1
    EXIT FUNCTION
END IF

A = INSTR(A$, "'" + ">>> Start of page")
IF A THEN
    Analyze = 2
    CheckSum = A    ' use to pass it to Mr. Filter
    EXIT FUNCTION
END IF

Analyze = 4
FOR A = 1 TO 20
    Ch$ = MID$(A$, A, 1)
    IF LEN(Ch$) THEN
        Ch = ASC(Ch$)
        SELECT CASE Ch
            CASE 10, 13
            CASE IS < 32
                Analyze = 3: EXIT FOR
            CASE IS > 127
                HiASCII = HiASCII + 1
        END SELECT
    ELSE EXIT FOR
    END IF
NEXT
IF HiASCII > 12 THEN Analyze = 3

END FUNCTION

FUNCTION CheckForFile& ()

OPEN SourceFile$ FOR BINARY AS #1
A& = LOF(1)
IF A& = 0 THEN
    CLOSE
    KILL SourceFile$
    COLOR 7: PRINT "   File not found."
END IF
CheckForFile& = A&

END FUNCTION

SUB ExtractFile ()
SHARED Good$

COLOR 7: PRINT : PRINT "Examining "; SourceFile$; "..."

ON ERROR GOTO ErrorRead

CLOSE : OPEN SourceFile$ FOR INPUT AS #1 LEN = 4096
SEEK #1, CheckSum
LINE INPUT #1, A$   'remove start line
LINE INPUT #1, A$

Temp = INSTR(A$, ",1,")
IF Temp = 0 THEN GOTO ErrorReading
NewFile$ = MID$(A$, Temp + 4)
OPEN NewFile$ FOR BINARY AS #2

PRINT "Loading "; SourceFile$; "..."

LINE INPUT #1, A$   'remove T$
DO
    IF EOF(1) THEN GOTO ErrorReading

    LINE INPUT #1, A$

    SELECT CASE LEFT$(A$, 1)
        CASE "G"
            IF NOT QuoteOn THEN
                A$ = MID$(A$, 3)
                IF RIGHT$(A$, 1) = Qt$ THEN A$ = LEFT$(A$, LEN(A$) - 1)

                FOR Q = 2 TO 9       ' expand the string
                    Look$ = MID$(ComprChar$, Q - 1, 1)
                    S = 1
                    DO
                        S = INSTR(S, A$, Look$)
                        IF S THEN
                            A$ = LEFT$(A$, S - 1) + STRING$(Q, 97) + MID$(A$, S + 1)
                        END IF
                    LOOP WHILE S
                NEXT

                Dat$ = Dat$ + RTRIM$(A$)
            END IF
        CASE "'"

            QuoteOn = NOT QuoteOn
        CASE ELSE                ' just comments or junk
            IF NOT QuoteOn THEN
                IF (MID$(A$, 2, 1) = "=") AND INSTR(A$, "Bad") THEN EXIT DO
            END IF
    END SELECT
LOOP

n = VAL(MID$(A$, 3))             ' extract size of file

Temp = INSTR(A$, "$)<>")
IF Temp = 0 THEN GOTO ErrorReading
IF LEN(Dat$) <> VAL(MID$(A$, Temp + 4)) THEN GOTO ErrorReading
LINE INPUT #1, A$
LINE INPUT #1, A$
LINE INPUT #1, A$
CheckVal = VAL(MID$(A$, 8))
CLOSE #1

PRINT "Decoding "; SourceFile$; "..."
PRINT STRING$(50, 178);     ' print initial bar
LOCATE , , 0

k = 255: V! = 50 / n

FOR A = 1 TO n          ' decode file
    IF L = 0 THEN
        GOSUB G: L = 6
        LOCATE , 1: PRINT STRING$(V! * A, 177);
    END IF

    W = T \ Shift(6 - L): GOSUB G: W = W OR T * Shift(L)
    L = L - 2: B$ = CHR$(W AND k)
    PUT 2, , B$
NEXT

PRINT
PRINT
IF (C = CheckVal) AND (LOF(2) = n) THEN
    PRINT NewFile$; " successfully extracted."
ELSE
    PRINT "Bad checksum or incomplete script!"
END IF

CLOSE
END

G:
    I = I + 1: T = INSTR(Good$, MID$(Dat$, I, 1)) - 1
    C = (C + T) * 2: C = C \ 256 + (C AND 255)
RETURN

ErrorReading:
    PRINT "Error reading script."
    END
END SUB

FUNCTION GetInformation ()

    '**** Remark the below for QBasic ***
Temp$ = LTRIM$(RTRIM$(COMMAND$))

ShortCopyright

DO
    IF LEN(Temp$) = 0 THEN
        SourceFile$ = UCASE$(GetInput$("Input filename (text/binary)? ", -1))
    ELSE
        SourceFile$ = Temp$: Temp$ = ""
    END IF

    IF LEN(SourceFile$) THEN A& = CheckForFile ELSE END
LOOP UNTIL A&
PRINT : DefaultFile$ = ParseFileName$

Recommend = Analyze(SourceFile$)
IF Recommend <= 2 THEN GetInformation = Recommend: EXIT FUNCTION

COLOR 15: PRINT "I recommend using the ";
COLOR 13
IF Recommend = 3 THEN
    PRINT "binary script (Y)";
    R$ = "Y"
ELSE

    PRINT "message wrapper (N)";
    R$ = "N"
END IF
COLOR 15: PRINT " on this file."

WhatFmt$ = UCASE$(GetInput$("Which format [" + R$ + "]? ", 1))
IF (WhatFmt$ <> "Y") AND (WhatFmt$ <> "N") THEN WhatFmt$ = R$
LOCATE CSRLIN - 1, 19
PRINT WhatFmt$

IF WhatFmt$ = "Y" THEN
    IF A& > 24000 THEN
        COLOR 7: PRINT
        PRINT "Sorry -- PostIt! doesn't support huge scripts yet."
        END
    END IF
    Recommend = 3
    FileLength = A&
ELSE
    Recommend = 4
END IF

A$ = "What is the destination prefix (max. 6 chars.) ["
DestFile$ = UCASE$(GetInput$(A$ + DefaultFile$ + "]? ", 6))
IF LEN(DestFile$) = 0 THEN
    DestFile$ = DefaultFile$
    LOCATE CSRLIN - 1, 52 + LEN(DefaultFile$)
    PRINT DefaultFile$
END IF

PRINT
IF Recommend = 4 THEN
    TabStops = VAL(GetInput$("Expand tabs to how many spaces [4]? ", 1))
    IF TabStops <= 0 THEN
        TabStops = 4
        LOCATE CSRLIN - 1, 36
        PRINT TabStops
    END IF
END IF

PageLength = VAL(GetInput$("Page length [85]? ", 3))
IF PageLength < 5 THEN
    PageLength = 85
    LOCATE CSRLIN - 1, 19
    PRINT "85 "
END IF

LinesOut$ = GetInput$("Lines to reserve on first message [5]? ", 2)
LinesOut = VAL(LinesOut$)
IF (LEN(LinesOut$) = 0) OR (LinesOut < 0) THEN
    LinesOut = 5
    LOCATE CSRLIN - 1, 40
    PRINT "5 "
END IF

LOCATE , , 0
GetInformation = Recommend

END FUNCTION

FUNCTION GetInput$ (Prompt$, MaxLen)

Null$ = CHR$(0): SpaceBar$ = " "
IF MaxLen < 1 THEN MaxLen = 80 - LEN(Prompt$) - POS(0)

COLOR 14: PRINT Prompt$;
StartX = POS(0): Cursor = 1
COLOR 7

DO
    IF Updt THEN
        LOCATE , StartX, 0
        PRINT OutS$; SpaceBar$;
        Updt = False
    END IF

    LOCATE , Cursor + StartX - 1, 1, 0, 16
    DO: I$ = INKEY$
    LOOP UNTIL LEN(I$)

    IF LEN(I$) = 1 THEN
        Updt = True

        SELECT CASE ASC(I$)
         CASE IS >= 32
            IF (LEN(OutS$) < MaxLen) OR (NOT Insrt AND (Cursor<= MaxLen)) THEN
                IF Cursor > 0 THEN
                    OutS$ = LEFT$(OutS$, Cursor - 1) + I$ + MID$(OutS$, Cursor - (NOT Insrt))
                ELSE
                    OutS$ = I$
                END IF
                Cursor = Cursor + 1
            ELSE
                Updt = False
            END IF
        CASE 8
            IF LEN(OutS$) AND (Cursor > 1) THEN
                OutS$ = LEFT$(OutS$, Cursor - 2) + MID$(OutS$, Cursor)
                Cursor = Cursor - 1
            ELSE
                Updt = False
            END IF
        CASE 13
            EXIT DO
        CASE 27
            IF LEN(OutS$) > 0 THEN
                LOCATE , StartX, 0
                PRINT SPACE$(LEN(OutS$) + 1);

                OutS$ = ""
                Cursor = 1
                Updt = False
            ELSE
                EXIT DO
            END IF
        END SELECT
    END IF
LOOP

LOCATE , , 1, 0, 16: PRINT
GetInput$ = LTRIM$(RTRIM$(OutS$))

END FUNCTION

SUB Initialize ()

LOCATE , , 0
FOR DefShift = 0 TO 6: Shift(DefShift) = 2 ^ DefShift: NEXT

ComprChar$ = "()*+,-./": Proplr$ = CHR$(179) + "/-\"
Qt$ = CHR$(34): A$ = " "

CurrentPage = 1: CurrentBit = 0: Char = 0

END SUB

SUB JustDoIt ()

SEEK #1, 1
LinesOut = LinesOut + 2     ' compensate for header
TotalLinesOut = 3
DO
    CurrentByte = SEEK(1)
    L& = FileLength - CurrentByte + 1 ' what's left?
    SELECT CASE L&
        CASE IS > 4096
            Block$ = SPACE$(4096)
        CASE IS <= 0
            EXIT DO
        CASE ELSE
            Block$ = SPACE$(L&)     ' rest of it
    END SELECT
    GET #1, , Block$

    FOR Pointr = 1 TO LEN(Block$)
        IF (Pointr AND 15) = 0 THEN
            CurrentByte = CurrentByte + 16
            Twirl
        END IF
        PutBytes ASC(MID$(Block$, Pointr, 1))
    NEXT
LOOP

    'flush the input buffer if it contains any bits
IF CurrentBit > 0 THEN
    CurrentBit = -1: PutByte Char
END IF

IF aLength > 0 THEN
    IF aLength = 1 THEN
        Work$ = Work$ + "a"
    ELSE
        Work$ = Work$ + MID$(ComprChar$, aLength - 1, 1)
    END IF
END IF

IF LEN(Work$) > 2 THEN
    'flush the line buffer if it contains any characters
    PrintLine Work$ + Qt$
END IF

END SUB

SUB MrFilter ()

Temp = INSTR(DefaultFile$, ".")
IF Temp THEN
    D$ = LEFT$(DefaultFile$, Temp) + ".OUT"
ELSE
    D$ = DefaultFile$ + ".OUT"
END IF

DestFile$ = UCASE$(GetInput$("Output filename [" + D$ + "]? ", 6))
IF LEN(DestFile$) = 0 THEN
    DestFile$ = D$
    LOCATE CSRLIN - 1, 21 + LEN(D$), 0
    PRINT D$
END IF

CLOSE : OPEN SourceFile$ FOR INPUT AS #1
OPEN DestFile$ FOR OUTPUT AS #2
SEEK #1, CheckSum

PRINT : PRINT "Working...";

Flip = 1
ChopOut = False

DO WHILE NOT EOF(1)
    LINE INPUT #1, L$
    L$ = RTRIM$(L$)

    IF LEN(L$) THEN
        IF ASC(L$) = 39 THEN
            IF LEFT$(L$, 22) = "'>>> Continued on page" THEN
                ChopOut = True
                SEEK #2, SEEK(2) - 2
            ELSEIF LEFT$(L$, 18) = "'>>> Start of page" THEN
                ChopOut = False
                IF SEEK(1) <> Start THEN SEEK #1, SEEK(1) + 2
            ELSEIF LEFT$(L$, 12) = "'________O_/" THEN
                ChopOut = True
            ELSE
                IF NOT ChopOut THEN ProcessLine L$
            END IF
        ELSEIF NOT ChopOut THEN
            IF NOT ChopOut THEN ProcessLine L$
        END IF
    ELSE
        IF NOT ChopOut THEN PRINT #2,
    END IF
LOOP
CLOSE                       ' close the files

LOCATE , 1
PRINT "Complete!      "
END

END SUB

SUB MsgSplit (Filename$, TheName$, OutN$, LPP, Reserve)

CLOSE : OPEN Filename$ FOR INPUT AS #1

Tab$ = CHR$(9)
LinesOut = Reserve + 1
FileOutNum = 1: OnMsgNumber = 1
LPP = LPP - 4               ' lines per page
LOFile& = LOF(1)

Base$ = LEFT$(OutN$, 6)

COLOR 7, 0: PRINT
DO
    OutN$ = Base$ + Num2Str$(FileOutNum)

    IF Row THEN LOCATE Row, Col: PRINT "         "
    PRINT "Now writing: "; OutN$; ".PI ";
    Row = CSRLIN: Col = POS(0)

    OPEN OutN$ + ".PI" FOR OUTPUT AS #2

    IF OnMsgNumber > 1 THEN
        PRINT #2, "'>>> Start of page"; STR$(OnMsgNumber); "."
        PRINT #2,
    ELSE
        GOSUB Snip
        PRINT #2, "'This file created by PostIt! v6.1."
        PRINT #2, "'>>> Start of page"; STR$(OnMsgNumber); "."
        PRINT #2,
    END IF

    TooLong = False
    FOR Trans = LinesOut TO LPP
        IF (Trans AND 3) = 0 THEN
            Percent = (100& * SEEK(1)) \ LOFile&
            Twirler$ = MID$(Proplr$, (Percent AND 3) + 1, 1)
            LOCATE Row, Col: PRINT USING "! ###%"; Twirler$; Percent;
        END IF

        IF NOT EOF(1) THEN
            IF Trans = LinesOut THEN
                DO
                    IF EOF(1) THEN
                        CLOSE
                        KILL OutN$ + ".PI"
                        OutN$ = Base$ + Num2Str$(FileOutNum - 1)
                        OPEN OutN$ + ".PI" FOR APPEND AS #2
                        SEEK #2, LOF(2) - 26 - (FileOutNum > 9)
                        GOSUB Snip
                        CLOSE
                        EXIT DO
                    END IF
                    LINE INPUT #1, Buf$
                LOOP WHILE LEN(Buf$) = 0
                IF LEN(Buf$) = 0 THEN EXIT DO
            ELSE
                LINE INPUT #1, Buf$
                Buf$ = RTRIM$(Buf$)
            END IF

            Tb = INSTR(Buf$, Tab$)  'remove chr$(8)s (tabs)
            IF Tb THEN
                DO
                    Temp = (Tb - 1) MOD TabStops
                    IF Temp = 0 THEN Temp = TabStops
                    Buf$ = LEFT$(Buf$, Tb - 1) + SPACE$(TabStops - Temp) + MID$(Buf$, Tb + 1)
                    Tb = INSTR(Tb, Buf$, Tab$)
                LOOP WHILE Tb
            END IF

Wrapping:
            IF (LEN(Buf$) > LineLength) AND (LEFT$(Buf$, 1) <> "'") THEN
                Trans = Trans + 1
                CommentOn = False
                FOR A = LineLength TO 40 STEP -1
                    IF MID$(Buf$, A, 1) = " " THEN
                        WrapPoint = A
                        EXIT FOR
                    END IF
                NEXT
                IF WrapPoint = 0 THEN WrapPoint = LineLength

                QuotesOn = False
                FOR A = 1 TO WrapPoint
                    Temp$ = MID$(Buf$, A, 1)
                    IF Temp$ = Qt$ THEN
                        QuotesOn = NOT QuotesOn
                    ELSEIF NOT QuotesOn THEN
                        IF (Temp$ = "'") OR (UCASE$(MID$(Buf$, A, 4)) = "REM ") THEN
                            CommentOn = True
                            EXIT FOR
                        END IF
                    END IF
                NEXT

                Long$ = Buf$
                IF CommentOn THEN
                    Buf$ = LEFT$(Buf$, WrapPoint - 1)
                ELSE
                    IF QuotesOn THEN
                        Buf$ = LEFT$(Buf$, WrapPoint - 1) + Qt$ + "+_"
                    ELSE
                        Buf$ = LEFT$(Buf$, WrapPoint - 1) + "_"
                    END IF
                END IF

                IF NOT ((Trans = LPP) AND LEN(Buf$) = 0) THEN
                    PRINT #2, Buf$
                END IF

                Buf$ = MID$(Long$, WrapPoint)
                IF CommentOn THEN Buf$ = "'" + Buf$
                IF QuotesOn THEN Buf$ = Qt$ + Buf$

                GOTO Wrapping
            END IF

            IF NOT ((Trans = LPP) AND LEN(Buf$) = 0) THEN
                PRINT #2, Buf$
            END IF
        END IF
    NEXT
    IF NOT EOF(1) THEN
        PRINT #2,
        PRINT #2, "'>>> Continued on page"; OnMsgNumber + 1

        OnMsgNumber = OnMsgNumber + 1
        FileOutNum = FileOutNum + 1
        LinesOut = 1
    ELSE
        PRINT #2,
        GOSUB Snip
        PRINT #2,
    END IF

    CLOSE #2
LOOP UNTIL EOF(1)
CLOSE

LOCATE Row, Col
PRINT "         "
PRINT
PRINT "Complete!"
END

Snip:
    PRINT #2, "'______O_/__________________| SNIP |__________________\_O______"
    PRINT #2, "'      O \                  | HERE |                  / O"
RETURN

END SUB

FUNCTION Num2Str$ (A)
    Num2Str$ = MID$(STR$(A), 2)
END FUNCTION

FUNCTION ParseFileName$ ()

FOR S = LEN(SourceFile$) TO 1 STEP -1
    IF INSTR("\:", MID$(SourceFile$, S, 1)) THEN EXIT FOR
NEXT
RealSource$ = MID$(SourceFile$, S + 1)

Ext = INSTR(RealSource$, ".")
IF Ext <> 0 THEN
    DestTemp$ = LEFT$(RealSource$, Ext - 1)
ELSE
    DestTemp$ = RealSource$
END IF

ParseFileName = UCASE$(LEFT$(DestTemp$, 7))

END FUNCTION

SUB PrepareFile ()

F$ = UCASE$(DestFile$ + Num2Str$(CurrentPage) + ".BAS")
CheckSum = 0

COLOR 7: PRINT
PRINT "Now writing: "; F$; " ";
Row = CSRLIN: Col = POS(0)

OPEN F$ FOR OUTPUT AS #2 LEN = 8192     ' use 8K buffer

PRINT #2, "C";
PRINT #2, "LS:?STRING$(50,178):DEFINT A-Z 'Created by PostIt! 6.1"
PRINT #2, "FOR A=0 TO 6:P(A)=2^A:NEXT:OPEN "; Qt$; "B"; Qt$; ",1,"; Qt$; RealSource$
PRINT #2, "T$="; Qt$; "abcdefghijklmnopqrstuvwxyz"; Qt$; ":T$=T$+UCASE$(T$)+"; Qt$; "0123456789#$"

Prefix$ = "G" + Qt$
Work$ = Prefix$

END SUB

SUB PrintDecoder ()

PrintLine "N=" + Num2Str$(FileLength) + ":K=255:IF LEN(C$)<>" +_
 Num2Str$(BytesOut) + " THEN ?" + Qt$ + "Bad script!" + Qt$ +_
 ":END"
PrintLine "FOR A=1 TO N:LOCATE 1:?STRING$(50/N*A,177):IF L=0"+_
" THEN GOSUB G:L=6"
PrintLine "W=T\P(6-L):GOSUB G:W=W OR T*P(L):L=L-2:B$=CHR$(W AND"+_
" K):PUT 1,,B$:NEXT"
PrintLine "?:IF C=" + Num2Str$(CheckSum) + " THEN ?" + Qt$ +_
 "Ok" + Qt$ + ":END ELSE ?" + Qt$ + "Bad checksum!" + Qt$ +_
 ":END"
PrintLine "G:I=I+1:T=INSTR(T$,MID$(C$,I,1))-1:C=(C+T)*2:C=C"+_
"\256+(C AND 255):RETURN"
PrintLine "SUB G(A$):SHARED C$:FOR Q=2 TO"+_
" 9:DO:S=INSTR(A$,CHR$(Q+38))"
PrintLine "IF S THEN A$=LEFT$(A$,S-1)+STRING$(Q,97)+MID$(A$,S+1)"
PrintLine "LOOP WHILE S:NEXT:C$=C$+A$:END SUB"
CLOSE

END SUB

'Outputs one line to the output file, and opens another output file
'if the page length is exceeded.
SUB PrintLine (A$)
STATIC NewFileFlag

IF NewFileFlag THEN
    LOCATE Row, Col: PRINT "          "

    NewFileFlag = False
    CurrentPage = CurrentPage + 1
    B$ = Num2Str$(CurrentPage)
    PRINT #2, "'>> Continued on pg. "; B$
    CLOSE #2

    F$ = UCASE$(DestFile$ + B$ + ".BAS")

    PRINT "Now writing: "; F$; " ";
    Row = CSRLIN: Col = POS(0)

    OPEN F$ FOR OUTPUT AS #2 LEN = 8192

    PRINT #2, "'>> Start: pg. "; B$
    LinesOut = 1
END IF

PRINT #2, A$

TotalLinesOut = TotalLinesOut + 1
LinesOut = LinesOut + 1
IF LinesOut >= PageLength THEN NewFileFlag = True

END SUB

SUB ProcessLine (In$) STATIC   ' belongs to MrFilter

CONST Blank = " ", Plus = "+"

    IF Shave THEN
        In$ = MID$(In$, 2)
        Shave = False
    END IF

    In$ = Previous$ + In$
    Previous$ = ""
    IF ASC(RIGHT$(In$, 1)) = 95 THEN
        IF LEN(In$) > 2 THEN
            SELECT CASE LEFT$(RIGHT$(In$, 2), 1)
                CASE Blank
                CASE Plus
                    Previous$ = LEFT$(In$, LEN(In$) - 3)
                    Shave = True
                CASE ELSE
                    Previous$ = LEFT$(In$, LEN(In$) - 1)
            END SELECT
        END IF
    END IF

    IF LEN(Previous$) = 0 THEN
        PRINT #2, In$
    END IF

    LOCATE , 12
    PRINT MID$(Proplr$, Flip + 1, 1);
    Flip = (Flip + 1) AND 3

END SUB

'Adds a character to the output string.
SUB PutByte (A)
    SHARED Good$

IF CurrentBit < 0 THEN LastOne = True

BytesOut = BytesOut + 1

    'calculate a checksum on the encoded data stream
CheckSum = (CheckSum + A) * 2
CheckSum = CheckSum \ 256 + (CheckSum AND 255)

IF (A = 0) AND (LastOne = False) THEN
    IF aLength = 9 THEN
        aLength = 1
        Work$ = Work$ + "/"
    ELSE
        aLength = aLength + 1
    END IF
ELSE
    SELECT CASE aLength
    CASE 0
        'translate the output character into something safe
        Work$ = Work$ + MID$(Good$, A + 1, 1)
    CASE 1
        Work$ = Work$ + "a" + MID$(Good$, A + 1, 1)
        aLength = 0
    CASE ELSE
        Work$ = Work$ + MID$(ComprChar$, aLength - 1, 1) +_
 MID$(Good$, A + 1, 1)
        aLength = 0
   END SELECT
END IF

IF LEN(Work$) >= LineLength THEN
    IF LEN(Work$) = LineLength THEN
        PrintLine Work$
        Work$ = Prefix$
    ELSE
        PrintLine LEFT$(Work$, LineLength)
        Work$ = Prefix$ + MID$(Work$, LineLength + 1)
    END IF
END IF

END SUB

SUB PutBytes (A)

    'shift the 8 bit character into the work buffer
Char = Char + A * Shift(CurrentBit)

    'we've got 8 more bits now
CurrentBit = CurrentBit + 8

    'write the 6 bit codes now
DO WHILE CurrentBit > 5          'have at least 6 bits left?
    PutByte Char AND 63          'write out the first 6 bits
    Char = Char \ 64             'shift it right 6 places
    CurrentBit = CurrentBit - 6  '6 bits less now
LOOP

END SUB

SUB ShortCopyright ()

COLOR 15, 0
CLS

PRINT "ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»"
PRINT "º   PostIt! 6.1   THE Binary <-> BASIC Script Creator   º"
PRINT "ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶"
PRINT "º      Rich Geldreich, Jim Giordano, Mark H Butler,     º"
PRINT "º   Quinn Tyler Jackson, Scott Wunsch, and Victor Yiu.  º"
PRINT "ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼"
PRINT
COLOR 12
PRINT "PostIt! 6.1 can:"
COLOR 13
PRINT "  o  Encode binary files as text"
PRINT "  o  Split messages and wrap lines"
PRINT "  o  Extract binary scripts"
PRINT "  o  Filter split messages to original state"
PRINT

END SUB

SUB Twirl () STATIC

LOCATE Row, Col
PRINT MID$(Proplr$, Turn + 1, 1);
Turn = (Turn + 1) AND 3

IF Turn = 0 THEN
    PRINT USING " ###%"; 100& * CurrentByte \ FileLength;
END IF

END SUB


'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O

'That's all, folks!  All you have to do to get PostIt! 6.1 working is to
'clump all the messages together, headers and all, and run them through
'Mr. Filter.  Fortunately (and unfortunately for me -- I've just killed
'another one of my programs <G>  i.e. MessageSplit), it will be the last
'time you'll have to use it.  Everything should be able to be automated
'with PostIt!.

'



Msg #:  5682                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-03-93 21:38
   To:  ALL                       Rcvd: -NO-
   Re:  FILTERHIGH 2.0 (1/4)

-----------------------------------
Use the FH.OBJ file and do this:

lib fh +fh;
link /qui fh.lib,,,\qb\bqlb45;
                       ^^^^^^--- use appropriate one...
Then you will get the QLB and the LIB file.
------------------------------------
Below is the FH.ASM...

; FilterHigh 2.0
; ~~~~~~~~~~~~~~
; Ultra-quick filtering routine, written in assembly.
;
; 1.0  John Gallas     Original release
; 2.0  Victor Yiu      ASM Version
;
; declare:
; DECLARE SUB FilterHighASM (BYVAL Segm%, BYVAL Offst%, BYVAL Leng%)

CODE SEGMENT PARA PUBLIC 'CODE'
    PUBLIC FilterHighASM
    assume cs:CODE, ds:nothing, es:nothing, ss:nothing

FilterHighASM PROC FAR

JMP NEAR Start

Table LABEL BYTE
db 0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,19,20,21,22
db 23,24,25,26,27,28,29,30,31,' !"#$%&',39,'()*+,-./0123456789:'
db ';<=>?@ABCDEFGHIJKLMNOPQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstu'
db 'vwxyz{|}~oCueaaaaceeeiiiAAE&AooouuyOUcLY#faiounNao?++//!<>!'
db '@#|++++++|+++++++++-++++++++=+++++++++++++#v||^ab%nEeur*OOQ'
db 'oo{N=#><///=^../n2o '

EVEN
Start:
    PUSH BP
    MOV BP, SP      ; set up stack frame

    PUSH SI         ; save required registers
    PUSH DI
    PUSH DS

    MOV DX, [BP+6]  ; load # of bytes into DX
    LDS SI, [BP+8]  ; load string addresses into DS/SI
    LES DI, [BP+8]  ; and ES/DI

    MOV BX, OFFSET Table  ; point BX to the table offset for XLAT

    MOV AX, DX      ; save count into AX
    MOV CL, 4       ; 2^4 = 16, shift count
    SHR DX, CL      ; divide count by sixteen -- each loop does 16 bytes
    MOV CX, DX      ; put it into CX, the counter var.

    AND AX, 15      ; take modulo 16 of saved count
    JZ InLineStart  ; if zero, just stop counting and start

    INC CX          ; otherwise, compensate for extra pass for loop
    SHL AX, 1       ; x4 -- 4 bytes of code for each byte processed
    SHL AX, 1
    MOV DX, OFFSET InLineEnd    ; find end of in-line code
    SUB DX, AX      ; figure where to jump to
    JMP DX          ; jump!

EVEN                ; align to even addr -- faster!
InLineStart:

REPT 16             ; repeat 16 times for speed!
    LODSB           ; load byte
    XLAT [CS:BX]    ; translate
    STOSB           ; store
ENDM

InLineEnd:
LOOP InLineStart

Quit:
    POP DS          ; restore registers
    POP DI
    POP SI
    POP BP
    RET 6           ; return, shaving off 6 bytes

FilterHighASM ENDP
    CODE ENDS
END


MSGTOSS (continued on NEXT message)

Msg #:  5683                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-03-93 21:38
   To:  ALL                       Rcvd: -NO-
   Re:  FILTERHIGH 2.0 (1/4)

MSGTOSS (continued from LAST message)

-------8<---  Chop

BASIC & Object file in next message...


--- Blue Wave/RA v2.12 [NR]
 * Origin: Hard Disc Cafe | Houston Texas | (713) 589-2690 | 
(1:106/30.0)


Msg #:  5684                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-03-93 21:38
   To:  ALL                       Rcvd: -NO-
   Re:  FILTERHIGH 2.0 (2/4)

FH.BAS  (demonstration and testing program)
'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O
'This file created by PostIt! v6.1.
'>>> Start of page 1.

' FilterHigh 2.0
' ~~~~~~~~~~~~~~
' Ultra-quick filtering routine, written in assembly.
'
' 1.0  John Gallas     Original release
' 2.0  Victor Yiu      ASM Version -- FAST!
'
' Testing shows:  PC/4.77MHz  --> 6.2 times faster!
'                486DX/34MHz  --> 2.1 times faster!
'
DECLARE SUB FilterHighASM (BYVAL Segm%, BYVAL Offst%, BYVAL Leng%)
DECLARE SUB FilterHigh (Dat$)       ' call this...

DECLARE SUB OldFilterHigh (Text$)   ' these two are used for
DECLARE FUNCTION RandomGen$ (Num%)  ' demonstration purposes only

DEFINT A-Z      ' **** COMPILE BEFORE RUNNING TEST for accuracy
CONST TestLen = 4096

PRINT : PRINT "Testing... please wait..."

A$ = RandomGen(TestLen)

T! = TIMER
FOR X = 1 TO 400: B$ = A$: FilterHigh B$: NEXT
T! = TIMER - T!

A$ = RandomGen(TestLen)
O! = TIMER
FOR X = 1 TO 100: B$ = A$: OldFilterHigh A$: NEXT
O! = TIMER - O!

T! = 400 / T! * TestLen
O! = 100 / O! * TestLen

PRINT
PRINT USING "ASM: #,###,### bytes"; T!
PRINT USING "BAS: #,###,### bytes"; O!
PRINT USING "... in other words.... ##.# times faster_!"; T! / O!

SUB FilterHigh (Dat$)

IF LEN(Dat$) = 0 THEN EXIT SUB

' QB version
FilterHighASM VARSEG(Dat$), SADD(Dat$), LEN(Dat$)

' VBDOS/PDS version
'FilterHighASM SSEG(Dat$), SADD(Dat$), LEN(Dat$)

END SUB

SUB OldFilterHigh (Text$) STATIC

IF NOT Init THEN
    DIM Table(0 TO 255)
    Table(128) = ASC("C"): Table(129) = ASC("u"): Table(130) =
ASC("e")
    Table(131) = ASC("a"): Table(132) = ASC("a"): Table(133) =
ASC("a")
    Table(134) = ASC("a"): Table(135) = ASC("c"): Table(136) =
ASC("e")
    Table(137) = ASC("e"): Table(138) = ASC("e"): Table(139) =
ASC("i")
    Table(140) = ASC("i"): Table(141) = ASC("i"): Table(142) =
ASC("A")

'>>> Continued on page 2 


--- Blue Wave/RA v2.12 [NR]
 * Origin: Hard Disc Cafe | Houston Texas | (713) 589-2690 | 
(1:106/30.0)


Msg #:  5685                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-03-93 21:39
   To:  ALL                       Rcvd: -NO-
   Re:  FILTERHIGH 2.0 (3/4)

'>>> Start of page 2.

    Table(143) = ASC("A"): Table(144) = ASC("E"): Table(145) =
ASC("&")
    Table(146) = ASC("A"): Table(147) = ASC("O"): Table(148) =
ASC("o")
    Table(149) = ASC("o"): Table(150) = ASC("u"): Table(151) =
ASC("u")
    Table(152) = ASC("y"): Table(153) = ASC("O"): Table(154) =
ASC("U")
    Table(155) = ASC("c"): Table(156) = ASC("L"): Table(159) =
ASC("f")
    Table(160) = ASC("a"): Table(161) = ASC("i"): Table(162) =
ASC("o")
    Table(163) = ASC("u"): Table(164) = ASC("n"): Table(165) =
ASC("N")
    Table(166) = ASC("a"): Table(167) = ASC("o"): Table(174) =
ASC("<")
    Table(175) = ASC(">"): Table(179) = ASC("|"): Table(180) =
ASC("+")
    Table(181) = ASC("+"): Table(182) = ASC("+"): Table(183) =
ASC("+")
    Table(184) = ASC("+"): Table(185) = ASC("+"): Table(186) =
ASC("|")
    Table(187) = ASC("+"): Table(188) = ASC("+"): Table(189) =
ASC("+")
    Table(190) = ASC("+"): Table(191) = ASC("+"): Table(192) =
ASC("+")
    Table(193) = ASC("+"): Table(194) = ASC("+"): Table(195) =
ASC("+")
    Table(196) = ASC("-"): Table(197) = ASC("+"): Table(198) =
ASC("+")
    Table(199) = ASC("+"): Table(200) = ASC("+"): Table(201) =
ASC("+")
    Table(202) = ASC("+"): Table(203) = ASC("+"): Table(204) =
ASC("+")
    Table(205) = ASC("="): Table(206) = ASC("+"): Table(207) =
ASC("+")
    Table(208) = ASC("+"): Table(209) = ASC("+"): Table(210) =
ASC("+")
    Table(211) = ASC("+"): Table(212) = ASC("+"): Table(213) =
ASC("+")
    Table(214) = ASC("+"): Table(215) = ASC("+"): Table(216) =
ASC("+")
    Table(217) = ASC("+"): Table(218) = ASC("+"): Table(228) =
ASC("E")
    Table(246) = ASC("/"): Table(248) = ASC("o"): Table(252) =
ASC("n")
    Table(253) = ASC("2")
END IF

'IF ASC(User.IBMGraph) THEN
'   FilterHigh$ = Text$
'   EXIT FUNCTION
'END IF

DEF SEG = VARSEG(Text$)
ptr = SADD(Text$)

FOR z = 1 TO LEN(Text$)

   IF PEEK(ptr) > 128 THEN
      IF Table(PEEK(ptr)) THEN
         POKE ptr, Table(PEEK(ptr))
      ELSE
         POKE ptr, 35
      END IF
   END IF

   ptr = ptr + 1

NEXT z

END SUB

FUNCTION RandomGen$ (Num)

A$ = SPACE$(Num)
FOR X = 1 TO Num
    IF RND > .7 THEN
        MID$(A$, X) = CHR$(RND * 128)
    ELSE
        MID$(A$, X) = CHR$(RND * 128 + 127)
    END IF
NEXT

RandomGen$ = A$

END FUNCTION


MSGTOSS (continued on NEXT message)

Msg #:  5686                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-03-93 21:39
   To:  ALL                       Rcvd: -NO-
   Re:  FILTERHIGH 2.0 (3/4)

MSGTOSS (continued from LAST message)

'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O

Now, people without MASM capture the next message:

Victor


--- Blue Wave/RA v2.12 [NR]
 * Origin: Hard Disc Cafe | Houston Texas | (713) 589-2690 | 
(1:106/30.0)


Msg #:  5687                      QUIKBAS Subboard
 From:  VICTOR YIU                Sent: 06-03-93 21:39
   To:  ALL                       Rcvd: -NO-
   Re:  FILTERHIGH 2.0 (4/4)

>> Run this through PostIt! 6.1!

CLS:?STRING$(50,178):DEFINT A-Z 'Created by PostIt! 6.1
FOR A=0 TO 6:P(A)=2^A:NEXT:OPEN "B",1,"FH.OBJ
T$="abcdefghijklmnopqrstuvwxyz":T$=T$+UCASE$(T$)+"0123456789#$
G"as(cyesSB5b)bd9erfreMh(A5fGaceGEqsb(eqdgLetuvKuiL0rif0unb)CiO9f
G"q)q6be(biWaeuGbhGqckSadn4WdqeHetqrfwCbgzOXgC0HhFasiImcjLyYjOKIk
G"RWslU8cmXiZm0uJn3Gto6Sdp94ZpafKqdrurgDesjP0sm1Ktpbvusnfvvz1vyLL
G"wBXvxE9fyHj2yKvMzNHwAQTgBT52BWfNCZrxD2DhE5P3E81NFVnuDLfwyHf2yLv
G"wzPLwAbfurMe0BV9wD1L3tvngtznIzHL2B15MtH92pRSYlVecp#ecqJW3kRSYkR
G"ScFRSYkRSYkRSYkTSYkRSYkRSYk9SYkRSYkRSYkRSYkRSYi2XhFEfMyL4wrLvNC
G"Q80tr92B75upJ4dpV8Yl94LlU8IBY8giqw1ISB1vESOvguSDiqSFiS7(Ki0XsW0
G"QVOYL8(01qqrdE0GRlCbSc0$loKS6Y1QYQlxRkRUCTQS6Y1QYQlxRkRUCTQS6Y1
G"QYQlxRkRUCTQS6Y1QYQlxRkRUCTQS6Y1QYQlxRkRUCTQS6Y1QkUVF8LxDPSbaGp
G"NjaqXuqvafNcvbOUIc)0b"
N=451:K=255:IF LEN(C$)<>602 THEN ?"Bad script!":END
FOR A=1 TO N:LOCATE 1:?STRING$(50/N*A,177):IF L=0 THEN GOSUB G:L=6
W=T\P(6-L):GOSUB G:W=W OR T*P(L):L=L-2:B$=CHR$(W AND K):PUT 1,,B$:NEXT
?:IF C=179 THEN ?"Ok":END ELSE ?"Bad checksum!":END
G:I=I+1:T=INSTR(T$,MID$(C$,I,1))-1:C=(C+T)*2:C=C\256+(C AND
255):RETURN
SUB G(A$):SHARED C$:FOR Q=2 TO 9:DO:S=INSTR(A$,CHR$(Q+38))
IF S THEN A$=LEFT$(A$,S-1)+STRING$(Q,97)+MID$(A$,S+1)
LOOP WHILE S:NEXT:C$=C$+A$:END SUB

'


 From:  IAN REMMLER               Sent: 05-31-93 21:37
   To:  CALVIN FRENCH             Rcvd: -NO-
   Re:  PLASMA GENERATOR

Well, here goes -
It's really pretty simple. - alot simpler than trying to use a bunch o'
nested loops like I did at first (stupid, stupid, STUPID!). Oh well,
here it is.

DECLARE SUB Adjust (xa, ya, x, y, xb, yb)
DECLARE SUB SubDivide (x1, y1, x2, y2)

SCREEN 13
RANDOMIZE TIMER
GOSUB PalSet

PSET (0, 0), (RND * 255) + 1
PSET (319, 0), (RND * 255) + 1
PSET (319, 199), (RND * 255) + 1
PSET (0, 199), (RND * 255) + 1

CONST F = 1.5  'change this to vary roughness
CALL SubDivide(0, 0, 319, 199)
BEEP
DO: LOOP WHILE INKEY$ = ""
END

PalSet:
  FOR a = 0 TO 63
    s = 0: r = 63: g = a: b = 0: GOSUB Set
    s = 64: r = 63 - a: g = 63: b = 0: GOSUB Set
    s = 128: r = 0: g = 63 - a: b = a: GOSUB Set
    s = 192: r = a: g = 0: b = 63: GOSUB Set
  NEXT
RETURN
Set:
  IF a + s = 0 THEN RETURN  'to keep the background black
  OUT &H3C8, a + s
  OUT &H3C9, r
  OUT &H3C9, g
  OUT &H3C9, b
RETURN

SUB Adjust (xa, ya, x, y, xb, yb)
  IF POINT(x, y) <> 0 THEN EXIT SUB
  d = ABS(xa - xb) + ABS(ya - yb)
  v = (POINT(xa, ya) + POINT(xb, yb)) / 2 + (RND - .5) * d * F
  IF v < 1 THEN v = 1
  IF v > 255 THEN v = 255
  PSET (x, y), v
END SUB

SUB SubDivide (x1, y1, x2, y2)
  IF (x2 - x1 < 1) AND (y2 - y1 < 1) THEN EXIT SUB
  x = (x1 + x2) / 2
  y = (y1 + y2) / 2
  CALL Adjust(x1, y1, x, y1, x2, y1)
  CALL Adjust(x2, y1, x2, y, x2, y2)
  CALL Adjust(x1, y2, x, y2, x2, y2)
  CALL Adjust(x1, y1, x1, y, x1, y2)
  IF POINT(x, y) = 0 THEN v = (POINT(x1, y1) + POINT(x2, y1) +_
  POINT(x2, y2) + POINT(x1, y2) + POINT(x1, y) + POINT(x, y1) +_
  POINT(x2, y) + POINT(x, y2)) / 8: PSET (x, y), v
  CALL SubDivide(x1, y1, x, y)
  CALL SubDivide(x, y1, x2, y)
  CALL SubDivide(x, y, x2, y2)
  CALL SubDivide(x1, y, x, y2)
END SUB

'It's dirt slow so don't run it unless you won't need your computer for
'say, 10 min. or so. -
'
'


Msg #:  5734                      QUIKBAS Subboard
 From:  ROMMIE BREWER             Sent: 06-04-93 23:08
   To:  ZACK JONES                Rcvd: -NO-
   Re:  REGISTRATION KEY PT1 OF 5

'________O_/________________________| SNIP
|______________________\_O_______
'        O \                        | HERE |                      / O
'This file created by PostIt! v6.0.
'>>> Start of page 1.

' A key-file generation program follows
' Zack,
'   As promised 87 years ago, here is a simple key-file generation
' program.  It is designed to keep honest people honest, as any
' hacker can break it by either breaking the code or patching the
' original program to bypass the registration checking.
'   As written, this will generate a simple key and includes the
' code to check that the key can be decoded.  Several things need
' to be done before it is used in 'real life'.  I'll list them in a
' minute.

' What it does:
'   1 - Generates a key file that includes a CRC check and an
'       embedded registration name and serial number.
'     - The first two lines of this file show the registration
'       name and serial number.  These lines are not used by the
'       program and can be changed without affecting the programs
'       operation as long as total line length is not changed.
'       They are included so you can do a quick check of who that
'       key is for.  This allows you to make several keys at once
'       and then sort out who gets which one (you would need to
'       include a routine to change the key file name after each
'       generation.
'     - The remaining space is filled by randomly generated ASCII
'       characters, with the TIMER function used to seed the random
'       generator.
'     - The display name and serial number are then encrypted and
'       the letters scattered about the random ASCII.
'     - A 16 bit CRC check is performed, and the value is encrypted
'       and and put into an area not included in the CRC check.
'
'   2 - Generates a historical record, with enough information to
'       generate an identical key at a later date. (This prevents a
'       couple of people from registering a program and getting a
'       key, then requesting a replacement key and comparing the
'       differences in order to break the encryption.)
'     - This data includes the registration name, serial number,
'       date the key is generated, and the seed for the random
'       generator.
'
' What it needs to be usable:
'   1 - Better routines for getting the display name and serial
'       number.  I decided to not waste bandwidth on examples that
'       others have already made.
'   2 - Larger areas for the display name and serial number.  I
'       limited these also for space
'   3 - Places for an address in the historical file
'   4 - Routines to compare names and serial numbers for dupes
'   5 - Routine to look through historical file and select one and
'       generate a replacement key based on the information found.
'   6 - A field for different levels of registration.  That is easy
'       to add using the procedures demonstrated.
'   7 - A drop-dead date for temporary keys.  I suggest that the
'       number of days since some arbitrary date be selected as the
'       base date (1 Jan 1900 ??) and then a value be added with
'       the days after the base date as the drop dead date.  Using
'       the same basedate in the generator and the actual program,
'       an imbedded 'total days' number can be made with each temp
'       key.  Use the system date to get 'current total days'.
'       This prevents someone from hacking a new month into the
'       temp key.
'   8 - Change the encryption value of 64 to 'your' value, between
'       64 and 100.
' So, without further comment (HA!), here it is.  Comments?

' Onwards....


'------------------
' generate registration keys for programs

DECLARE FUNCTION crc16% (target$)

' define structure file 1 - which holds your list of past keys
TYPE KeyRecord
   Regno AS STRING * 10
   RegName AS STRING * 30
   Datereg AS STRING * 10
   Rndseed AS LONG
   LnTrn AS STRING * 2

END TYPE
DIM FileBuffer AS KeyRecord
  FileBuffer.LnTrn = CHR$(13) + CHR$(10)
DIM namepoint(20), serpt(20)
namlength = 5
seriallength = 5

' open file 1 as past keys
CLS

GOSUB oldkey

GOSUB getrandseed:  ' get a seed value for the random function

GOSUB opnkey: ' open the new KeyFile.Dat to write in the values

' get display name for key file.  Replace this routine with a better one
INPUT "What display name do you want to use "; Dspnam$
Dspnam$ = LEFT$(Dspnam$ + SPACE$(namlength), seriallength)

' get serial/registration number.  Replace this routine, also.
INPUT "What is the serial number "; srnmbr$
srnmbr$ = LEFT$(srnmbr$ + SPACE$(seriallength), seriallength)

' check on dupes of names and numbers

' get date of registration
   FileBuffer.Datereg = DATE$

' put info into file one and update
   FileBuffer.Regno = srnmb$
   FileBuffer.RegName = Dspnam$
   FileBuffer.Rndseed = rseed
   FileBuffer.LnTrn = CHR$(13) + CHR$(10)
   totrec = totrec + 1
   PUT #1, totrec, FileBuffer
   GET #1, 1, FileBuffer
   FileBuffer.Rndseed = totrec
   PUT #1, 1, FileBuffer


' generate key - file 2

' pad name with spaces to center
   namspac = LEN(Dspnam$)
   namfre = 80 - namspac - 2
   line1$ = SPACE$(namfre / 2) + Dspnam$ + SPACE$(namfre / 2) +_
 CHR$(13) + CHR$(10)
' put in Key File for your info only.  You use to confirm which key you
' are sending to who, by using a doc viewer
LSET fuline$ = line1$
PUT #2, 1

' pad serial with spaces to center
   serspac = LEN(srnmbr$)
   serfre = 80 - serspac - 2
   line2$ = SPACE$(serfre / 2) + srnmbr$ + SPACE$(serfre / 2) +_
 CHR$(13) + CHR$(10)

  ' put in file 2 as second line
LSET fuline$ = line2$
PUT #2, 2

' close out the two lines and re-open data file as 1 byte
GOSUB keyfill

  ' fill file 2 with random values
RANDOMIZE (-rseed)

  FOR x = 161 TO 500
      LSET PtFilr$ = CHR$(RND * 255)
      PUT #2, x
   NEXT x

' read locations for name letters
RESTORE namdatpt

  FOR x = 1 TO namlength
     READ namepoint(x)
  NEXT x

 FOR x = 1 TO namlength
'   convert name digit coded letter
  mp$ = CHR$((ASC(MID$(Dspnam$, x, 1)) + 64))
  LSET PtFilr$ = mp$
   PUT #2, namepoint(x)
 NEXT x

' read location for serial number
RESTORE serldatpt
  FOR x = 1 TO seriallength
    READ serpt(x)
  NEXT x

 FOR x = 1 TO seriallength
   sp$ = CHR$((ASC(MID$(srnmbr$, x, 1)) + 64))
   LSET PtFilr$ = sp$
   PUT #2, serpt(x)
 NEXT x

' calculate the CRC
testcr$ = ""
 FOR x = 161 TO 450
 GET #2, x
 testcr$ = testcr$ + PtFilr$
NEXT x

' calculate the crc, convert to a string so you can hide it
crcnumber = crc16(testcr$)
PRINT "crc checks as "; crcnumber
crcname$ = STR$(crcnumber)
crcname$ = LEFT$(LTRIM$(crcname$) + "aAbBcCdDeEfFgGhHiIjJkKlL",_
 10)

'PRINT "crc word = "; crcname$; "  and value "; VAL(crcname$)
' put the CRC at point 460 , incrementing the value of each letter
'   so it doesn't stand out as a number
FOR x = 460 TO 469
  LSET PtFilr$ = CHR$(ASC(MID$(crcname$, x - 459, 1)) + 64)
  PUT #2, x
NEXT x

' ----
' This is the part that would be in the program being protected.  It
' is put here to demonstrate the program works.
' The data points and file opening routines would need to be copied,
' also.


' retrieve the stored CRC
rechk$ = ""
FOR x = 460 TO 469
  GET #2, x
  rechk$ = rechk$ + CHR$(ASC(PtFilr$) - 64)
NEXT x
crcchk2 = VAL(rechk$):  ' the stored CRC value


' calculate the CRC
testcr$ = ""
 FOR x = 161 TO 450
 GET #2, x
 testcr$ = testcr$ + PtFilr$
NEXT x
crcnumber = crc16(testcr$)

IF crcchk2 = crcnumber THEN
  PRINT "They match as "; crcnumber
     Dspnam$ = ""
     FOR x = 1 TO namlength
'      convert digit coded letter to name
       GET #2, namepoint(x)
       mp$ = CHR$((ASC(PtFilr$) - 64))
       Dspnam$ = Dspnam$ + mp$
     NEXT x
       PRINT "Display Name is "; Dspnam$

  ELSE PRINT "No Match: something was changed ";
       PRINT crcnumber; " "; crcchk2

END IF

CLOSE
END


oldkey:
CLOSE #1
OPEN "oldkey.dat" FOR RANDOM AS #1 LEN = LEN(FileBuffer)
GET #1, 1, FileBuffer
  ' check if there is a data file.  If not, start one.
  IF INSTR(FileBuffer.Regno, "Start") = 0 THEN
    FileBuffer.Regno = "Start"
    FileBuffer.RegName = "No-Name"
    FileBuffer.Datereg = DATE$
    FileBuffer.Rndseed = 1
    FileBuffer.LnTrn = CHR$(13) + CHR$(10)
    PUT #1, 1, FileBuffer
    totrec = 1
  END IF
totrec = FileBuffer.Rndseed:  ' total registrations on file

RETURN


opnkey: ' open the new key file
CLOSE #2
OPEN "NewKey.DAT" FOR RANDOM AS #2 LEN = 80
  FIELD #2, 80 AS fuline$
RETURN

keyfill:
CLOSE #2
OPEN "NewKey.dat" FOR RANDOM AS #2 LEN = 1
FIELD #2, 1 AS PtFilr$
RETURN



getrandseed: ' get the random seed
rseed = INT(TIMER)
rseed = ABS(rseed)

RETURN

' below are the data areas where you specify the location inside the random
' generated area for the storage of your values.  For demo purposes, I am
' limiting the number of values so it is easy to visually check there are
' not any locations specified twice.  In actual practice, I suggest you
' write a random list - in order - on a piece of paper and scratch the
' values off as you put them here.

namdatpt: ' random data points for the name
DATA 241, 152, 423, 367, 275

serldatpt: ' random locations for the serial number
DATA 342, 467, 199, 300, 400

FUNCTION crc16% (target$)
STATIC Initialized%, CRCTable%()
' 05-25-93  Douglas Lusher  16bit CRC calculation  1:282/7
IF Initialized% GOTO CalcCRC16

REDIM CRCTable%(255)
FOR Ptr% = 0 TO 255
  CRC& = Ptr% * &H100&
  FOR Bit% = 0 TO 7
    Carry% = ((CRC& AND &H8000) <> 0)
    'Carry% is True if Bit 16 is set
    CRC& = (CRC& * 2) AND &HFFFF&
    'shift the low 16 bits one place left
    CRC& = CRC& XOR (Carry% AND &H1021)
    'if there was a carry, then XOR in the bitmask
  NEXT
  CRCTable%(Ptr%) = (CRC& - 32768) XOR &H8000
  'change the long int to an unsigned int for the table
NEXT
Initialized% = -1

CalcCRC16:

HiByte% = 0
LoByte% = 0
FOR Ptr% = 1 TO LEN(target$)
  Char% = ASC(MID$(target$, Ptr%))
  CRC& = CRCTable%(HiByte% XOR Char%) XOR LoByte%
  CRC& = CRC& * &H100
  HiByte% = (CRC& AND &HFF0000) \ &H10000
  LoByte% = ((CRC& AND &HFF00&) - 32768) XOR &H8000
NEXT
crc16% = HiByte% OR LoByte%

END FUNCTION
'


' From:  RICH GELDREICH            Sent: 06-08-93 03:03
'   To:  CALVIN FRENCH             Rcvd: -NO-
'   Re:  GIF LOADER/1

'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O
'This file created by PostIt! v6.1.
'>>> Start of page 1.
 
'
'DEGIF6.BAS - No frills GIF decoder for the VGA's 320x200x256 mode.
'By Rich Geldreich 1993 (Public domain, use as you wish.)
'This version should properly decode all LZW encoded images in
'GIF image files. I've finally added GIF89a and local colormap
'support, so it more closely follows the GIF specification. It
'still doesn't support the entire GIF89a specification, but it'll
'show most GIF files fine.
'The GIF decoding speed of this program isn't great, but I'd say
'for an all QB/PDS decoder it's not bad!
'Note: This program does not stop decoding the GIF image after the
'rest of the scanlines become invisible! This happens with images
'larger than the 320x200 screen. So if the program seems to be
'just sitting there, accessing your hard disk, don't worry...
'It'll beep when it's done.
DEFINT A-Z
'Prefix() and Suffix() hold the LZW phrase dictionary.
'OutStack() is used as a decoding stack.
'ShiftOut() as a power of two table used to quickly retrieve the LZW
'multibit codes.
DIM Prefix(4095), Suffix(4095), OutStack(4095), ShiftOut(8)
 
'The following line is for the QB environment(slow).
DIM YBase AS LONG, Powersof2(11) AS LONG, WorkCode AS LONG
'For a little more speed, unremark the next line and remark the one
'above, before you compile... You'll get an overflow error if the
'following line is used in the QB environment, so change it back.
'DIM YBase AS INTEGER, Powersof2(11) AS INTEGER, WorkCode AS INTEGER
 
'Precalculate power of two tables for fast shifts.
FOR A = 0 TO 8: ShiftOut(8 - A) = 2 ^ A: NEXT
FOR A = 0 TO 11: Powersof2(A) = 2 ^ A: NEXT
 
'Get GIF filename.
A$ = COMMAND$: IF A$ = "" THEN INPUT "GIF file"; A$: IF A$ = ""_
 THEN END
'Add GIF extension if the given filename doesn't have one.
FOR A = LEN(A$) TO 1 STEP -1
    SELECT CASE MID$(A$, A, 1)
    CASE "\", ":": EXIT FOR
    CASE ".": Extension = -1: EXIT FOR
    END SELECT
NEXT
IF Extension = 0 THEN A$ = A$ + ".GIF"
 
'Open file for input so QB stops with an error if it doesn't exist.
OPEN A$ FOR INPUT AS #1: CLOSE #1
OPEN A$ FOR BINARY AS #1
 
'Check to see if GIF file. Ignore GIF version number.
A$ = "      ": GET #1, , A$
IF LEFT$(A$, 3) <> "GIF" THEN PRINT "Not a GIF file.": END
 
'Get logical screen's X and Y resolution.
GET #1, , TotalX: GET #1, , TotalY: GOSUB GetByte
'Calculate number of colors and find out if a global palette exists.
NumColors = 2 ^ ((A AND 7) + 1): NoPalette = (A AND 128) = 0
'Retrieve background color.
GOSUB GetByte: Background = A
 
'Get aspect ratio and ignore it.
GOSUB GetByte
 
'Retrieve global palette if it exists.
IF NoPalette = 0 THEN P$ = SPACE$(NumColors * 3): GET #1, , P$
 
DO 'Image decode loop
 
'Skip by any GIF extensions.
'(With a few modifications this code could also fetch comments.)
DO
    'Skip by any zeros at end of image (why must I do this? the
    'GIF spec never mentioned it)
    DO
        IF EOF(1) THEN EXIT DO 'if at end of file, exit
        GOSUB GetByte
    LOOP WHILE A = 0           'loop while byte fetched is zero
 
    SELECT CASE A
    CASE 44  'We've found an image descriptor!
        EXIT DO
    CASE 59  'GIF trailer, stop decoding.
        GOTO AllDone
    CASE IS <> 33
        PRINT "Unknown GIF extension type.": END
    END SELECT
    'Skip by blocked extension data.
    GOSUB GetByte
    DO: GOSUB GetByte: A$ = SPACE$(A): GET #1, , A$: LOOP UNTIL_
 A = 0
LOOP
'Get image's start coordinates and size.
GET #1, , XStart: GET #1, , YStart: GET #1, , XLength: GET #1, ,_
 YLength
XEnd = XStart + XLength: YEnd = YStart + YLength
 
'Check for local colormap, and fetch it if it exists.
GOSUB GetByte
IF (A AND 128) THEN
    NoPalette = 0
    NumColors = 2 ^ ((A AND 7) + 1)
    P$ = SPACE$(NumColors * 3): GET #1, , P$
END IF
 
'Check for interlaced image.
Interlaced = (A AND 64) > 0: PassNumber = 0: PassStep = 8
 
'Get LZW starting code size.
GOSUB GetByte
 
'Calculate clear code, end of stream code, and first free LZW code.
ClearCode = 2 ^ A
EOSCode = ClearCode + 1
FirstCode = ClearCode + 2: NextCode = FirstCode
StartCodeSize = A + 1: CodeSize = StartCodeSize
 
'Find maximum code for the current code size.
StartMaxCode = 2 ^ (A + 1) - 1: MaxCode = StartMaxCode
 
BitsIn = 0: BlockSize = 0: BlockPointer = 1
 
X = XStart: y = YStart: YBase = y * 320&
 
'Set screen 13 in not set yet.
IF FirstTime = 0 THEN
    'Go to VGA mode 13 (320x200x256).
    SCREEN 13: DEF SEG = &HA000
END IF
 
'Set palette, if there was one.
IF NoPalette = 0 THEN
    'Use OUTs for speed.
    OUT &H3C8, 0
    FOR A = 1 TO NumColors * 3: OUT &H3C9, ASC(MID$(P$, A, 1)) \_
 4: NEXT
    'Save palette of image to disk.
    'OPEN "pal." FOR BINARY AS #2: PUT #2, , P$: CLOSE #2
END IF
 
IF FirstTime = 0 THEN
  'Clear entire screen to background color. This isn't
  'done until the image's palette is set, to avoid flicker
  'on some GIFs.
    LINE (0, 0)-(319, 199), Background, BF
    FirstTime = -1
END IF
 
'Decode LZW data stream to screen.
DO
    'Retrieve one LZW code.
    GOSUB GetCode
    'Is it an end of stream code?
    IF Code <> EOSCode THEN
        'Is it a clear code? (The clear code resets the sliding
        'dictionary - it *should* be the first LZW code present
        ' in the data stream.)
 
        IF Code = ClearCode THEN
            NextCode = FirstCode
            CodeSize = StartCodeSize
            MaxCode = StartMaxCode
            GOSUB GetCode
            CurCode = Code: LastCode = Code: LastPixel = Code
            IF X < 320 AND y < 200 THEN POKE X + YBase, LastPixel
            X = X + 1: IF X = XEnd THEN GOSUB NextScanLine
        ELSE
            CurCode = Code: StackPointer = 0
 
            'Have we entered this code into the dictionary yet?
            IF Code >= NextCode THEN
                IF Code > NextCode THEN GOTO AllDone 'Bad GIF if
                ' this happens.
                'mimick last code if we haven't entered the
                ' requested
                'code into the dictionary yet
                CurCode = LastCode
                OutStack(StackPointer) = LastPixel
                StackPointer = StackPointer + 1
            END IF
 
            'Recursively get each character of the string.
            'Since we get the characters in reverse, "push" them
            'onto a stack so we can "pop" them off later.
            'Hint: There is another, much faster way to
            ' accomplish
            'this that doesn't involve a decoding stack at all...
            DO WHILE CurCode >= FirstCode
                OutStack(StackPointer) = Suffix(CurCode)
                StackPointer = StackPointer + 1
                CurCode = Prefix(CurCode)
            LOOP
 
            LastPixel = CurCode
            IF X < 320 AND y < 200 THEN POKE X + YBase, LastPixel
            X = X + 1: IF X = XEnd THEN GOSUB NextScanLine
 
            '"Pop" each character onto the display.
            FOR A = StackPointer - 1 TO 0 STEP -1
                IF X < 320 AND y < 200 THEN POKE X + YBase, OutStack(A)
                X = X + 1: IF X = XEnd THEN GOSUB NextScanLine
            NEXT
 
            'Can we put this new string into our dictionary?
            ' (Some GIF
            'encoders will wait a bit when the dictionary is full
            'before sending a clear code- this increases
            ' compression
            'because the dictionary's contents are thrown away
            ' less
            'often.)
            IF NextCode < 4096 THEN
                'Store new string in the dictionary for later
                ' use.
                Prefix(NextCode) = LastCode
                Suffix(NextCode) = LastPixel
                NextCode = NextCode + 1
                'Time to increase the LZW code size?
                IF (NextCode > MaxCode) AND (CodeSize < 12) THEN
                    CodeSize = CodeSize + 1
                    MaxCode = MaxCode * 2 + 1
                END IF
            END IF
            LastCode = Code
        END IF
    END IF
LOOP UNTIL Code = EOSCode
 
LOOP
 
AllDone:
 
'Save image and palette to BSAVE file.
'DEF SEG = &HA000
'OUT &H3C7, 0
'FOR a = 0 TO 767
'    POKE a + 64000, INP(&HÃ9)
'NEXT
 
'BSAVE "pic.bas", 0, 64768
 
'Load images saved with the above code with this:
'DEF SEG= &HA000
'BLOAD "Pic.Bas"
'OUT &H3C8, 0
'FOR a = 0 To 767
'     OUT &H3C9, Peek(a+ 64000)
'NEXT
 
BEEP: DO: LOOP WHILE INKEY$ <> "": DO: LOOP UNTIL INKEY$ <> ""
END
 
'Slowly reads one byte from the GIF file...
GetByte: A$ = " ": GET #1, , A$: A = ASC(A$): RETURN
 
'Moves down one scanline. If the GIF is interlaced, then the number
'of scanlines skipped is based on the current pass.
NextScanLine:
    IF Interlaced THEN
        y = y + PassStep
        IF y >= YEnd THEN
            PassNumber = PassNumber + 1
            SELECT CASE PassNumber
            CASE 1: y = 4: PassStep = 8
            CASE 2: y = 2: PassStep = 4
            CASE 3: y = 1:ÐassStep = 2
            END SELECT
        END IF
    ELSE
        y = y + 1
    END IF
    X = XStart: YBase = y * 320&
RETURN
 
'Reads a multibit code from the data stream. Look ma, see how
'simple it is now!
GetCode:
    WorkCode = LastChar \ ShiftOut(BitsIn)
  'Loop while more bits are needed.
    DO WHILE CodeSize > BitsIn
'Reads a byte from the LZW data stream. Since the data stream is
'blocked, a check is performed for the end of the current block
'before each byte is fetched.
        IF BlockPointer > BlockSize THEN
          'Retrieve block's length
            GOSUB GetByte: BlockSize = A
            A$ = SPACE$(BlockSize): GET #1, , A$
            BlockPointer = 1
        END IF
      'Yuck, ASC() and MID$() aren't that fast.
        LastChar = ASC(MID$(A$, BlockPointer, 1))
        BlockPointer = BlockPointer + 1
      'Append 8 more bits to the input buffer
        WorkCode = WorkCode OR LastChar * Powersof2(BitsIn)
        BitsIn = BitsIn + 8
    LOOP
  'Take away x number of bits.
    BitsIn = BitsIn - CodeSize
  'Return code to caller.
    Code = WorkCode AND MaxCode
RETURN
 
'


' From:  RICH GELDREICH            Sent: 06-08-93 03:10
'   To:  VICTOR YIU                Rcvd: -NO-
'   Re:  PROTOTYPE 1/3

'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O
'This file created by PostIt! v6.1.
'>>> Start of page 1.
 
'Hi Victor! The following prototype creates the most advanced PostIt!
'script we've ever developed! It has the following features:
'1. Maximum filesize of 150k!
'2. VERY efficient encoding algorithm - much better than PostIt's
'   simple 6 bit scheme.
'3. A fast and simple decoding algorithm makes extraction very fast.
'   (I'm thinking about making an assembly decoder for it, since it's
'   so simple.)
'
'I'd like to note that the encoding algorithm of this program is
'even more efficient than Coridon Henshaw's BT8 encoder. It's also
'many times faster, too!
'
'I know you're busy because of those damn tests and all of your other
'projects, but if you incorporated all of the features of PostIt! 6.1
'with the features of this script and we would have one hell of a
'program.
'
DEFINT A-Z
 
DECLARE SUB EmptyBucket ()
DECLARE SUB EncodeBlock ()
DECLARE SUB EncodeEnd ()
DECLARE SUB EncodeStart ()
DECLARE SUB PrintLine (A$)
DECLARE SUB PrintScriptLine (A$)
 
DIM SHARED I$                       'Input file's name
DIM SHARED InputBuffer$, BytesRead  'Input buffer for fast reader
DIM SHARED OutputLine$, OutputPos, LinesWritten 'Output buffer
DIM SHARED NextSub, LinesInSub      'Current subroutine info
'Encoding vars
DIM SHARED FlagScaler, CurrentFlag, Bucket(1 TO 4), CodesInBucket
 
DIM BytesLeft AS LONG
 
IF POS(0) <> 1 THEN PRINT
PRINT "Yet Another PostIt! Prototype Script Encoder By Rich"+_
" Geldreich"
INPUT "Input file"; I$
INPUT "Output file"; O$
 
OPEN I$ FOR BINARY AS #1
BytesLeft = LOF(1)
IF BytesLeft = 0 THEN
    CLOSE
    KILL I$
    PRINT I$; " wasn't found."
    END
ELSEIF BytesLeft > (150 * 1024&) THEN
    CLOSE
    PRINT "Sorry, the input file must be less than 150k."
    END
END IF
 
OPEN O$ FOR OUTPUT AS #2 LEN = 4096
 
EncodeStart
 
InputBuffer$ = SPACE$(4096)
BytesRead = 4096
 
DO
    IF BytesLeft < 4096 THEN
        InputBuffer$ = SPACE$(BytesLeft)
        BytesRead = BytesLeft
    END IF
 
    GET #1, , InputBuffer$
 
    EncodeBlock
 
    LOCATE , 1
    PRINT LTRIM$(STR$(BytesLeft)); " bytes remaining    ";
 
    BytesLeft = BytesLeft - BytesRead
LOOP WHILE BytesLeft
 
EncodeEnd
 
LOCATE , 1
 
PRINT LTRIM$(STR$(LinesWritten)); " lines in"; NextSub; "sub(s)"
PRINT "Input:"; LOF(1); "bytes"
PRINT "Output:"; LOF(2); "bytes"
PRINT "Ratio:"; STR$((LOF(2) * 100&) \ LOF(1)); "%"
 
CLOSE 1, 2
 
END
 
SUB EmptyBucket
 
    IF CodesInBucket THEN
        MID$(OutputLine$, OutputPos) = CHR$(CurrentFlag + 35)
        OutputPos = OutputPos + 1
        IF OutputPos = 66 THEN PrintScriptLine OutputLine$
 
        FOR A = 1 TO CodesInBucket
            MID$(OutputLine$, OutputPos) = CHR$(Bucket(A) + 35)
            OutputPos = OutputPos + 1
            IF OutputPos = 66 THEN PrintScriptLine OutputLine$
        NEXT
    END IF
 
END SUB
 
SUB EncodeBlock
 
    FOR A = 1 TO BytesRead
 
        K = ASC(MID$(InputBuffer$, A, 1))
 
        CurrentFlag = CurrentFlag + (K \ 86) * FlagScaler
        FlagScaler = FlagScaler * 3
        CodesInBucket = CodesInBucket + 1
        Bucket(CodesInBucket) = (K MOD 86)
 
        IF CodesInBucket = 4 THEN
            EmptyBucket
            FlagScaler = 1
            CodesInBucket = 0
            CurrentFlag = 0
        END IF
 
    NEXT
 
END SUB
 
SUB EncodeEnd
 
    EmptyBucket
 
    IF OutputPos <> 3 THEN
        PrintScriptLine LEFT$(OutputLine$, OutputPos - 1)
    END IF
 
    IF LinesInSub <> -1 THEN
        PrintLine "END SUB"
    END IF
 
    'There must be a better way of doing this! One sub call per line
    'sucks. (QB doesn't like sub calls like this: V0:V1:V2)
    FOR A = 0 TO NextSub - 1
        PrintLine "V" + HEX$(A)
    NEXT
 
    'Look at this decoder! It still needs some work, but it's simple
    'and fast. (It needs a character translator, because it currently
    'uses characters like "@" which can cause problems on some
    'networks like the RIME. A little percent meter would also look
    'neat too.)
    L1$ = "SUB U(A$):FOR A=1 TO LEN(RTRIM$(A$)):C=ASC(MID$(A$,"+_
"A,1))-35"
    L2$ = "B=B-1:IF B<0 THEN B=4:K=C ELSE ?#1,CHR$(C+(K MOD"+_
" 3)*86);:K=K\3"
    L3$ = "NEXT: END SUB"
    L4$ = "CLOSE"
    PrintLine L1$
    PrintLine L2$
    PrintLine L3$
    PrintLine L4$
 
END SUB
 
SUB EncodeStart
 
    OutputLine$ = "U" + CHR$(34) + SPACE$(63)
    OutputPos = 3
 
    FOR A = LEN(I$) TO 1 STEP -1
        IF INSTR("\:", MID$(I$, A, 1)) THEN EXIT FOR
    NEXT
    P$ = UCASE$(MID$(I$, A + 1))
 
    Q$ = CHR$(34)
 
    L0$ = "'This is a prototype PostIt! self extracting script."
 
    L1$ = "DEFINT A-Z:OPEN" + Q$ + "O" + Q$ + ",1," + Q$ + P$ + Q$
    L1$ = L1$ + ",4^6:DIM SHARED B,K"
 
    PrintLine L0$
    PrintLine L1$
 
    NextSub = 0
    LinesInSub = -1
 
    FlagScaler = 1
    CurrentFlag = 0
    CodesInBucket = 0
 
END SUB
 
SUB PrintLine (A$)
 
    PRINT #2, A$
 
    LinesWritten = LinesWritten + 1
 
END SUB
 
SUB PrintScriptLine (A$)
 
    IF LinesInSub = -1 THEN
        LinesInSub = 0
        PrintLine "SUB V" + HEX$(NextSub)
        NextSub = NextSub + 1
    END IF
 
    PrintLine A$
    OutputPos = 3
 
    LinesInSub = LinesInSub + 1
    IF LinesInSub = 350 THEN
        PrintLine "END SUB"
        LinesInSub = -1
    END IF
 
END SUB
 
'



Msg #:  5954                      QUIKBAS Subboard
 From:  RICH GELDREICH            Sent: 06-08-93 03:15
   To:  ALL                       Rcvd: -NO-
   Re:  WIREFRAME 3-D 1/11

The following 11 messages contain a very cool object based wireframe 3-D
program I made a few months ago. It's pretty fast - even on a nice slow
286/10. It is keyboard controllable and fun to play with.  Zack Jones
gave me permission to post this a few weeks ago, so here it goes!
 
'_____O_/________________________| SNIP |______________________\_O____
'     O \                        | HERE |                      / O
'This file created by PostIt! v6.0.
'>>> Start of page 1.
 
'
'WIREF4.BAS By Rich Geldreich
'Last modified April 28, 1993.
'For PDS/VB-DOS only. This program isn't totally completed, and
'doesn't have much documentation, yet. I'd appreciate your
'feedback!
'
DEFINT A-Z
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
CONST True = -1, False = 0
CONST MaxObject = 9
CONST MaxPlane = 99
CONST MaxPoint = (MaxPlane + 1) * 3 - 1
CONST MaxLine = (MaxPlane + 1) * 3 - 1
CONST PerspectiveScaler& = 768
CONST RotateScaler = 2048
CONST UserPlane = 75
'Constants for SCREEN 9, the EGA's 640x350x16 two page mode.
CONST XScreenRatio = 5, YScreenRatio = 4
CONST MinX = 0, MinY = 0
CONST MaxX = 639, MaxY = 349
CONST MidX = 320, MidY = 175
CONST LineColor = 15
CONST ViewDistance& = 7000& * 7000
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
DEF FNV (A) = ((A MOD 360) + 360) MOD 360
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
TYPE VectType
    A1              AS INTEGER
    A2              AS INTEGER
    A3              AS INTEGER
END TYPE
 
TYPE OrgType
    Ox              AS INTEGER
    Oy              AS INTEGER
    Oz              AS INTEGER
END TYPE
 
TYPE SineCosType
    S1              AS LONG
    C1              AS LONG
    S2              AS LONG
    C2              AS LONG
    S3              AS LONG
    C3              AS LONG
END TYPE
 
TYPE PointType
    x               AS INTEGER
    y               AS INTEGER
    z               AS INTEGER
    Rx              AS INTEGER
    Ry              AS INTEGER
    Rz              AS INTEGER
END TYPE
 
TYPE ObjectType
    Org             AS OrgType
    Direction       AS VectType
    PlaneIndice     AS INTEGER
    PointIndice     AS INTEGER
    MaxPlane        AS INTEGER
    MaxPoint        AS INTEGER
    MaxCord         AS INTEGER
    CullFlag        AS INTEGER
END TYPE
 
TYPE PlaneType
    Points(0 TO 3)  AS INTEGER
    MaxPoint        AS INTEGER
END TYPE
 
TYPE LineType
    sx              AS INTEGER
    sy              AS INTEGER
    ex              AS INTEGER
    ey              AS INTEGER
END TYPE
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'Number of objects to read.
DATA 8
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Objects Follow--
 
'    To  speed  things  up  I  recommend that very large, complicated
'objects be split up  into  numerous  smaller objects because objects
'which are totally behind the viewer are ignored.  If most of a gaint
'object is visible, then the entire object must be processed.  If the
'object is built of smaller objects then less of it will be processed
'when part of it is behind the user.
 
'--Object 0, box.
'Object's starting XYZ coordinates.
DATA -60,0,-200
'Object's starting rotatation angles.
DATA 0,0,0
 
'    If this value not zero, then the object can be culled.  (Culling
'removes hidden polygons from the object to  speed  up  plotting  and
'improve  clarity.)  For  culling  to work properly all planes in the
'object must be specified  in  counter-clockwise  order as if you are
'looking directly at it!
DATA -1
 
'Planes
'    The first number specifies  the  number  of points in the plane.
'If the plane contains 4 points, then a 3 would appear as  the  first
'number  on  the  DATA statement(0-3=4 points).  Planes with 3 points
'would be proceeded with a  2.  The  remaining numbers point into the
'point list.  A plane may have 2,3,  or  4  points.   Planes  with  2
'points cannot be culled and are treated as single lines.
 
DATA 3,0,1,2,3
DATA 3,1,5,6,2
DATA 3,5,4,7,6
DATA 3,4,0,3,7
DATA 3,4,5,1,0
DATA 3,3,2,6,7
'End the plane list with -32768.
DATA -32768
 
'Points
'       Each  XYZ  point in the object follows.  The plane list above
'refers to this list.  A point  may  be shared by more than one plane
'in its object, but points cannot be shared between objects.
DATA -100,-100,100
DATA 100,-100,100
DATA 100,100,100
DATA -100,100,100
DATA -100,-100,-100
DATA 100,-100,-100
DATA 100,100,-100
DATA -100,100,-100
'End the point list with -32768,0,0.
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Object 1, box.
DATA 0,0,300, 0,0,0, -1
DATA 3,0,1,2,3, 3,1,5,6,2, 3,5,4,7,6, 3,4,0,3,7, 3,4,5,1,0,_
 3,3,2,6,7
DATA -32768
DATA -100,-100,100, 100,-100,100, 100,100,100, -100,100,100
DATA -100,-100,-100, 100,-100,-100, 100,100,-100, -100,100,-100
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Object 2, house.
DATA 0,0,0, 0,0,0, 0
DATA 3,0,1,2,3, 3,4,5,6,7, 1,1,5, 1,0,4, 1,3,7, 1,2,6
DATA -32768
DATA -1000,-400,1000, 1000,-400,1000, 1000,100,1000,_
 -1000,100,1000
DATA -1000,-400,-1000, 1000,-400,-1000, 1000,100,-1000,_
 -1000,100,-1000
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Object 3, doorway and sidewalk.
 
DATA 0,0,0, 0,0,0, 0
DATA 1,0,1, 1,2,3, 1,4,5, 1,6,7, 1,8,9
DATA -32768
DATA 150,100,1000, 150,-250,1000, -150,100,1000, -150,-250,1000
DATA -150,-250,1000, 150,-250,1000, -150,100,1000, -150,100,2500
DATA 150,100,1000, 150,100,2500
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Object 4, first window.
DATA 0,0,0, 0,0,0, 0
DATA 3,0,1,2,3
DATA -32768
DATA -500,-100,1000, -300,-100,1000, -300,-250,1000,_
 -500,-250,1000
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Object 5, second window.
DATA 0,0,0, 0,0,0, 0
DATA 3,0,1,2,3
DATA -32768
DATA 500,-100,1000, 300,-100,1000, 300,-250,1000, 500,-250,1000
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'--Object 6, pyramid.
DATA 0,100,3000, 0,0,0, -1
DATA 3,3,2,1,0, 2,4,2,3, 2,4,1,2, 2,4,0,1, 2,4,3,0
DATA -32768
DATA -300,0,-300, 300,0,-300, 300,0,300, -300,0,300, 0,-350,0
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
'Object 7, roof
DATA 0,0,0, 0,0,0, 0
DATA 1,0,4, 1,1,4, 1,2,4, 1,3,4
DATA -32768
DATA 1000,-400,-1000, -1000,-400,-1000
DATA -1000,-400,1000, 1000,-400,1000, 0,-800,0
DATA -32768,0,0
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
DIM SHARED SineTable(0 TO 359 + 90) AS LONG
DIM SHARED Objects(0 TO MaxObject) AS ObjectType
DIM SHARED Planes(0 TO MaxPlane) AS PlaneType
DIM SHARED Points(0 TO MaxPoint) AS PointType
DIM SHARED PlaneIndice, ObjectIndice, PointIndice
 
DIM SHARED WorldOrg AS OrgType
DIM SHARED WorldVect AS VectType
DIM SHARED WorldSineCos AS SineCosType
DIM SHARED WorldSpeed
 
DIM SHARED LinesToErase(0 TO 1, 0 TO MaxLine) AS LineType
DIM SHARED MaxLineToErase(0 TO 1)
 
DIM SHARED LowX, LowY, HighX, HighY
 
DIM SHARED VidPage
'-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-==-=-=-=-=-=-
PrintInstructions
InitializeTables
ReadObjects
InitializeWorld
 
LOCATE , 1
PRINT "Press any key!";
A$ = INPUT$(1)
DO
    A$ = INKEY$
    ProcessKey A$
    DoFrame
LOOP UNTIL A$ = CHR$(27)
END
 
'This function checks a plane to see if it can be  seen.   There  are
'faster  ways that don't involve all of this math, but this method is
'very elegant and easy to implement.
FUNCTION Check4Cull (BYVAL x0, BYVAL y0, BYVAL x1, BYVAL y1,_
 BYVAL x2, BYVAL y2)
    Check4Cull = (CLNG(x1 - x0) * (y2 - y0) - CLNG(x2 - x0) *_
 (y1 - y0)) >= 0
END FUNCTION
 
'This subroutine displays each object in the scene.
 
SUB DisplayObjects
    DIM ObjectVect AS VectType
    DIM ObjectSineCos AS SineCosType
    DIM ObjOrg AS PointType
 
    FOR A = 0 TO ObjectIndice
 
        ObjOrg.x = Objects(A).Org.Ox - WorldOrg.Ox
        ObjOrg.y = Objects(A).Org.Oy - WorldOrg.Oy
        ObjOrg.z = Objects(A).Org.Oz - WorldOrg.Oz
        RotateOrigPoint ObjOrg, WorldSineCos
 
        IF ObjOrg.Rz >= Objects(A).MaxCord THEN
 
            IF (CLNG(ObjOrg.x) * ObjOrg.x) + (CLNG(ObjOrg.y) *_
 ObjOrg.y) + (CLNG(ObjOrg.z) * ObjOrg.z) < ViewDistance& THEN
 
            ObjectVect = Objects(A).Direction
            IF ObjectVect.A1 = 0 AND ObjectVect.A2 = 0 AND_
 ObjectVect.A3 = 0 THEN
                FOR B = Objects(A).PointIndice TO_
 Objects(A).PointIndice + Objects(A).MaxPoint
                    RotateOrigPoint Points(B), WorldSineCos
                    Points(B).Rx = Points(B).Rx + ObjOrg.Rx
                    Points(B).Ry = Points(B).Ry + ObjOrg.Ry
                    Points(B).Rz = Points(B).Rz + ObjOrg.Rz
                NEXT
            ELSE
                LookUpSineCos ObjectVect, ObjectSineCos
                FOR B = Objects(A).PointIndice TO_
 Objects(A).PointIndice + Objects(A).MaxPoint
                    RotateOrigPoint Points(B), ObjectSineCos
                    Points(B).Rx = Points(B).Rx + ObjOrg.x
                    Points(B).Ry = Points(B).Ry + ObjOrg.y
                    Points(B).Rz = Points(B).Rz + ObjOrg.z
                    RotateNewPoint Points(B), WorldSineCos
                NEXT
            END IF
 
            I = MaxLineToErase(VidPage)
            LowX = 32767: LowY = 32767
            HighX = -32768: HighY = -32768
 
            IF Objects(A).CullFlag = True THEN
                FOR B = Objects(A).PlaneIndice TO_
 Objects(A).PlaneIndice + Objects(A).MaxPlane
                    ProjectPlane Planes(B)
                NEXT
            ELSE
                FOR B = Objects(A).PlaneIndice TO_
 Objects(A).PlaneIndice + Objects(A).MaxPlane
                    SELECT CASE Planes(B).MaxPoint
                    CASE 1
                        ProjectLine Points(Planes(B).Points(0)),_
 Points(Planes(B).Points(1))
                    CASE 2
                        ProjectLine Points(Planes(B).Points(0)),_
 Points(Planes(B).Points(1))
                        ProjectLine Points(Planes(B).Points(1)),_
 Points(Planes(B).Points(2))
                        ProjectLine Points(Planes(B).Points(2)),_
 Points(Planes(B).Points(0))
                    CASE ELSE
                        ProjectLine Points(Planes(B).Points(0)),_
 Points(Planes(B).Points(1))
                        ProjectLine Points(Planes(B).Points(1)),_
 Points(Planes(B).Points(2))
                        ProjectLine Points(Planes(B).Points(2)),_
 Points(Planes(B).Points(3))
                        ProjectLine Points(Planes(B).Points(3)),_
 Points(Planes(B).Points(0))
                    END SELECT
                NEXT
            END IF
 
            IF (LowX <= MaxX) AND (LowY <= MaxY) AND (HighX >=_
 0) AND (HighY >= 0) THEN
                FOR B = I + 1 TO MaxLineToErase(VidPage)
                    LINE (LinesToErase(VidPage, B).sx,_
 LinesToErase(VidPage, B).sy)-(LinesToErase(VidPage, B).ex,_
 LinesToErase(VidPage, B).ey), LineColor
                NEXT
            ELSE
                MaxLineToErase(VidPage) = I
            END IF
 
            END IF
 
        END IF
 
    NEXT
 
END SUB
 
SUB DoFrame
 
    UpdateObjects
    SwitchScreen
    EraseScreen
    DisplayObjects
 
END SUB
 
'This subroutine plots one line to the screen and enters it into the
'current page's erase list.
SUB DrawLine (BYVAL x0, BYVAL y0, BYVAL x1, BYVAL y1)
    DIM LineToPlot AS LineType
 
    IF x0 < LowX THEN LowX = x0
    IF y0 < LowY THEN LowY = y0
    IF x1 < LowX THEN LowX = x1
    IF y1 < LowY THEN LowY = y1
 
    IF x0 > HighX THEN HighX = x0
    IF y0 > HighY THEN HighY = y0
    IF x1 > HighX THEN HighX = x1
    IF y1 > HighY THEN HighY = y1
 
    LineToPlot.sx = x0
    LineToPlot.sy = y0
    LineToPlot.ex = x1
    LineToPlot.ey = y1
 
    A = MaxLineToErase(VidPage) + 1
    LinesToErase(VidPage, A) = LineToPlot
    MaxLineToErase(VidPage) = A
 
END SUB
 
'This subroutine erases all lines previously drawn on the current
'video page.
SUB EraseScreen
 
    FOR A = 0 TO MaxLineToErase(VidPage)
        LINE (LinesToErase(VidPage, A).sx, LinesToErase(VidPage,_
 A).sy)-(LinesToErase(VidPage, A).ex, LinesToErase(VidPage,_
 A).ey), 0
    NEXT
 
    MaxLineToErase(VidPage) = -1
END SUB
 
'This subroutine initializes the  sine  &  cosine lookup table.  Each
'entry is scaled up by a constant to avoid  floating  point  math  at
'runtime(in  assembly  this would already be calculated and stored as
'data.)
SUB InitializeTables
    FOR A = 0 TO 359
        SineTable(A) = INT(SIN(A / 57.2957) * RotateScaler + .5)
    NEXT
    FOR A = 360 TO 360 + 90 - 1
        SineTable(A) = SineTable(A - 360)
    NEXT
END SUB
 
'This subroutine initializes the variables used to describe the user's
'location and viewing angle.
SUB InitializeWorld
 
    WorldOrg.Ox = 0
    WorldOrg.Oy = -230
    WorldOrg.Oz = -600
    WorldVect.A1 = 0
    WorldVect.A2 = 0
    WorldVect.A3 = 0
 
    MaxLineToErase(0) = -1
    MaxLineToErase(1) = -1
    VidPage = 1
 
END SUB
 
'This function limits an integer into an inclusive range.
FUNCTION Limit (BYVAL A, BYVAL l, BYVAL H)
    IF A < l THEN A = l
    IF A > H THEN A = H
    Limit = A
END FUNCTION
 
FUNCTION LongLimit (BYVAL A&)
 
    IF A& >= -32768 AND A& <= 32767 THEN
        LongLimit = A&
    ELSE
 
        IF A& < 0 THEN
            LongLimit = -1
        ELSE
            LongLimit = MaxX + 1
        END IF
 
    END IF
 
END FUNCTION
 
'This subroutine takes a vector (3 angles) and looks them up in the
'sine & cosine table.
SUB LookUpSineCos (V AS VectType, A AS SineCosType)
    A.S1 = SineTable(V.A1)
    A.C1 = SineTable(V.A1 + 90)
 
    A.S2 = SineTable(V.A2)
    A.C2 = SineTable(V.A2 + 90)
 
    A.S3 = SineTable(V.A3)
    A.C3 = SineTable(V.A3 + 90)
END SUB
 
'This subroutine prints the instructions to the screen. (duh <g>)
SUB PrintInstructions
    PRINT "Simple Object Based Wireframe 3-D"
    PRINT "By Rich Geldreich (Zeek of Renaissance) April, 1993"
    PRINT "Use these keys to control position: (Turn NUMLOCK on!)"
    PRINT "4.............Turn Head Left"
    PRINT "6.............Turn Head Right"
    PRINT "8.............Go Forward"
    PRINT "9.............Go Backward"
    PRINT "5.............Stop motion"
    PRINT "A.............Total Reset"
    PRINT "Up Arrow......Turn Head Upward"
    PRINT "Down Arrow....Turn Head Downward"
    PRINT "Left Arrow....Tilt Head"
    PRINT "Right Arrow...Tilt Head"
    PRINT "U.............Y Coordinate -"
    PRINT "D.............Y Coordinate +"
    PRINT "L.............X Coordinate -"
    PRINT "R.............X Coordinate +"
    PRINT "ESC...........Quits"
    PRINT
    PRINT "Wait a sec!";
END SUB
 
'This subroutine gets called after each frame. It processes any
'keystrokes from the user and updates the location & viewing
'parameters.
SUB ProcessKey (A$) STATIC
 
    IF A$ <> "" THEN
        A = (ASC(RIGHT$(UCASE$(A$), 1))) * ((LEN(A$) > 1) OR 1)
        SELECT CASE A
        CASE 85
            WorldOrg.Oy = WorldOrg.Oy - 30
        CASE 68
            WorldOrg.Oy = WorldOrg.Oy + 30
        CASE 76
            WorldOrg.Ox = WorldOrg.Ox - 30
        CASE 82
            WorldOrg.Ox = WorldOrg.Ox + 30
        CASE 65
            WorldSpeed = 0
            A1 = 0: A2 = 0: A3 = 0
            WorldVect.A1 = 0
            WorldVect.A2 = 0
            WorldVect.A3 = 0
            WorldOrg.Ox = 0
            WorldOrg.Oy = -130
            WorldOrg.Oz = 0
        CASE -72 'up
            A3 = A3 - 3
        CASE -80 'down
            A3 = A3 + 3
        CASE -75 'left
            A2 = A2 + 3
        CASE -77 'right
            A2 = A2 - 3
        CASE 56  '8
            WorldSpeed = WorldSpeed - 15
        CASE 50  '2
            WorldSpeed = WorldSpeed + 15
        CASE 53, 32
            WorldSpeed = 0
            A1 = 0: A2 = 0: A3 = 0
        CASE 48
            A1 = 0: A2 = 0: A3 = 0
        CASE 52
            A1 = A1 - 3
        CASE 54
            A1 = A1 + 3
        END SELECT
        A1 = Limit(A1, -30, 30)
        A2 = Limit(A2, -30, 30)
        A3 = Limit(A3, -30, 30)
        WorldSpeed = Limit(WorldSpeed, -160, 160)
    END IF
 
    WorldVect.A1 = FNV(WorldVect.A1 + A1)
    WorldVect.A2 = FNV(WorldVect.A2 + A2)
    WorldVect.A3 = FNV(WorldVect.A3 + A3)
 
END SUB
 
'This  subroutine  takes  a  line  in  3-D  space  and calculates the
'starting and ending points of  the  line  on the viewing screen.  If
'the line passes the viewing plane, it is cut so the entire  line  is
'visible before the perspective calculation is applied.
SUB ProjectLine (p1 AS PointType, p2 AS PointType)
 
    x1 = p1.Rx
    y1 = p1.Ry
    z1 = p1.Rz
 
    x2 = p2.Rx
    y2 = p2.Ry
    z2 = p2.Rz
 
    IF (z1 < UserPlane) OR (z2 < UserPlane) THEN
        IF (z1 < UserPlane) AND (z2 < UserPlane) THEN EXIT SUB
 
        IF z1 < UserPlane THEN
            SWAP x1, x2
            SWAP y1, y2
            SWAP z1, z2
        END IF
 
        Xd& = x2 - x1
        Yd& = y2 - y1
        Zd& = z2 - z1
 
        z2 = UserPlane
        x2 = x1 + (Xd& * (UserPlane - z1)) \ Zd&
        y2 = y1 + (Yd& * (UserPlane - z1)) \ Zd&
    END IF
    sx = LongLimit(MidX + XScreenRatio * ((x1 *_
 PerspectiveScaler&) \ z1) \ 10)
    sy = LongLimit(MidY + YScreenRatio * ((y1 *_
 PerspectiveScaler&) \ z1) \ 10)
    ex = LongLimit(MidX + XScreenRatio * ((x2 *_
 PerspectiveScaler&) \ z2) \ 10)
    ey = LongLimit(MidY + YScreenRatio * ((y2 *_
 PerspectiveScaler&) \ z2) \ 10)
 
    DrawLine sx, sy, ex, ey
 
END SUB
 
SUB ProjectPlane (Plane AS PlaneType)
    DIM PointCut(0 TO 3)
 
    MP = Plane.MaxPoint
 
    IF MP = 1 THEN
        ProjectLine Points(Plane.Points(0)),_
 Points(Plane.Points(1))
        EXIT SUB
    END IF
 
    FOR A = 0 TO MP
        IF Points(Plane.Points(A)).Rz < UserPlane THEN
            PointCut(A) = True
            PointsCut = PointsCut + 1
        END IF
    NEXT
 
    IF PointsCut = 0 THEN
        p0 = Plane.Points(0): p1 = Plane.Points(1)
        p2 = Plane.Points(2): p3 = Plane.Points(3)
        SELECT CASE MP
        CASE 2
            ProjectPoint Points(p0), x0, y0
            ProjectPoint Points(p1), x1, y1
            ProjectPoint Points(p2), x2, y2
        CASE 3
            ProjectPoint Points(p0), x0, y0
            ProjectPoint Points(p1), x1, y1
            ProjectPoint Points(p2), x2, y2
            ProjectPoint Points(p3), x3, y3
        END SELECT
        IF Check4Cull(x0, y0, x1, y1, x2, y2) = False THEN
            SELECT CASE MP
            CASE 2
             DrawLine x0, y0, x1, y1
             DrawLine x1, y1, x2, y2
             DrawLine x2, y2, x0, y0
            CASE ELSE
             DrawLine x0, y0, x1, y1
             DrawLine x1, y1, x2, y2
             DrawLine x2, y2, x3, y3
             DrawLine x3, y3, x0, y0
            END SELECT
        END IF
    ELSEIF PointsCut - 1 = MP THEN
        EXIT SUB
    ELSE
 
        FOR A = 0 TO MP
            IF PointCut(A) = False THEN EXIT FOR
        NEXT
 
        LastP = (A - 1): IF LastP < 0 THEN LastP = MP
        NextP = (A + 1): IF NextP > MP THEN NextP = 0
 
        A = Plane.Points(A)
        LastP = Plane.Points(LastP)
        NextP = Plane.Points(NextP)
 
        SplitLine Points(A), Points(LastP), XL, YL
        SplitLine Points(A), Points(NextP), XN, YN
        ProjectPoint Points(A), XM, YM
 
        IF Check4Cull(XM, YM, XN, YN, XL, YL) = False THEN
            p0 = Plane.Points(0): p1 = Plane.Points(1)
            p2 = Plane.Points(2): p3 = Plane.Points(3)
            SELECT CASE MP
            CASE 2
                ProjectLine Points(p0), Points(p1)
                ProjectLine Points(p1), Points(p2)
                ProjectLine Points(p2), Points(p0)
            CASE ELSE
                ProjectLine Points(p0), Points(p1)
                ProjectLine Points(p1), Points(p2)
                ProjectLine Points(p2), Points(p3)
                ProjectLine Points(p3), Points(p0)
            END SELECT
        END IF
    END IF
END SUB
 
SUB ProjectPoint (P AS PointType, nx, ny)
 
    nx = LongLimit(MidX + XScreenRatio * ((P.Rx *_
 PerspectiveScaler&) \ P.Rz) \ 10)
    ny = LongLimit(MidY + YScreenRatio * ((P.Ry *_
 PerspectiveScaler&) \ P.Rz) \ 10)
 
END SUB
 
SUB ReadObjects
    RESTORE
    READ ObjectIndice
 
    PlaneIndice = 0
    PointIndice = 0
 
    FOR Object = 0 TO ObjectIndice - 1
        READ Objects(Object).Org.Ox
        READ Objects(Object).Org.Oy
        READ Objects(Object).Org.Oz
        READ Objects(Object).Direction.A1
        READ Objects(Object).Direction.A2
        READ Objects(Object).Direction.A3
        READ Objects(Object).CullFlag
 
        Objects(Object).PlaneIndice = PlaneIndice
        Objects(Object).PointIndice = PointIndice
 
        NumPlanes = 0
        DO
            READ A
            IF A <> -32768 THEN
                Planes(PlaneIndice).MaxPoint = A
                FOR B = 0 TO A
                    READ A
                    Planes(PlaneIndice).Points(B) = A +_
 PointIndice
                NEXT
                PlaneIndice = PlaneIndice + 1
                NumPlanes = NumPlanes + 1
            ELSE
                EXIT DO
            END IF
        LOOP
        Objects(Object).MaxPlane = NumPlanes - 1
 
        NumPoints = 0
        Max = -32768
        DO
            READ A, B, C
            IF A <> -32768 THEN
                IF ABS(A) > Max THEN Max = ABS(A)
                IF ABS(B) > Max THEN Max = ABS(B)
                IF ABS(C) > Max THEN Max = ABS(C)
                Points(PointIndice).x = A
                Points(PointIndice).y = B
                Points(PointIndice).z = C
                PointIndice = PointIndice + 1
                NumPoints = NumPoints + 1
            ELSE
                EXIT DO
            END IF
        LOOP
        Objects(Object).MaxPoint = NumPoints - 1
        Objects(Object).MaxCord = -(Max + 200)
    NEXT
    ObjectIndice = ObjectIndice - 1
 
    PlaneIndice = PlaneIndice - 1
    PointIndice = PointIndice - 1
END SUB
 
SUB RotateNewPoint (P AS PointType, A AS SineCosType)
 
    x1 = (P.Rx * A.C1 - P.Rz * A.S1) \ RotateScaler
    z1 = (P.Rx * A.S1 + P.Rz * A.C1) \ RotateScaler
 
    P.Rz = (z1 * A.C3 - P.Ry * A.S3) \ RotateScaler
    y2 = (z1 * A.S3 + P.Ry * A.C3) \ RotateScaler
 
    P.Rx = (x1 * A.C2 + y2 * A.S2) \ RotateScaler
    P.Ry = (y2 * A.C2 - x1 * A.S2) \ RotateScaler
 
END SUB
 
SUB RotateOrigPoint (P AS PointType, A AS SineCosType)
 
    x1 = (P.x * A.C1 - P.z * A.S1) \ RotateScaler
    z1 = (P.x * A.S1 + P.z * A.C1) \ RotateScaler
 
    P.Rz = (z1 * A.C3 - P.y * A.S3) \ RotateScaler
    y2 = (z1 * A.S3 + P.y * A.C3) \ RotateScaler
 
    P.Rx = (x1 * A.C2 + y2 * A.S2) \ RotateScaler
    P.Ry = (y2 * A.C2 - x1 * A.S2) \ RotateScaler
 
END SUB
 
SUB SplitLine (p1 AS PointType, p2 AS PointType, x0, y0)
 
    x1 = p1.Rx
    y1 = p1.Ry
    z1 = p1.Rz
 
    x2 = p2.Rx
    y2 = p2.Ry
    z2 = p2.Rz
 
    IF (z2 < UserPlane) THEN
 
        Xd& = x2 - x1
        Yd& = y2 - y1
        Zd& = z2 - z1
 
        z2 = UserPlane
        x2 = x1 + (Xd& * (UserPlane - z1)) \ Zd&
        y2 = y1 + (Yd& * (UserPlane - z1)) \ Zd&
 
    END IF
 
    x0 = LongLimit(MidX + XScreenRatio * ((x2 *_
 PerspectiveScaler&) \ z2) \ 10)
    y0 = LongLimit(MidY + YScreenRatio * ((y2 *_
 PerspectiveScaler&) \ z2) \ 10)
 
END SUB
 
SUB SwitchScreen
    VidPage = 1 - VidPage
    SCREEN 9, , VidPage, 1 - VidPage
    WAIT &H3DA, 8, 8
    WAIT &H3DA, 8
END SUB
 
SUB UpdateObjects
    STATIC Init, XMove, ZMove
 
    IF Init = False THEN
        XMove = 6
        ZMove = -4
        Init = True
    END IF
 
    Objects(1).Direction.A3 = FNV(Objects(1).Direction.A3 + 4)
    Objects(6).Direction.A1 = FNV(Objects(6).Direction.A1 - 4)
 
    x = Objects(1).Org.Ox
    x = x + XMove
    IF x < -800 OR x > 800 THEN XMove = -XMove: x = x + XMove
 
    Objects(1).Org.Ox = x
    z = Objects(1).Org.Oz
    z = z + ZMove
    IF z < -800 OR z > 800 THEN ZMove = -ZMove: z = z + ZMove
    Objects(1).Org.Oz = z
 
    mx = (WorldSpeed * WorldSineCos.C3) \ RotateScaler
    my = (WorldSpeed * WorldSineCos.S3) \ RotateScaler
    Mz = (mx * WorldSineCos.C1) \ RotateScaler
    mx = (mx * WorldSineCos.S1) \ RotateScaler
    WorldOrg.Ox = Limit(WorldOrg.Ox - mx, -16000, 16000)
    WorldOrg.Oy = Limit(WorldOrg.Oy + my, -16000, 16000)
    WorldOrg.Oz = Limit(WorldOrg.Oz - Mz, -16000, 16000)
    LookUpSineCos WorldVect, WorldSineCos
 
END SUB
 
 
'    That's all! Sorry that it only works under PDS or VB/DOS, but I love
'using BYVAL and having arrays in TYPE structures.

'


Msg #:  6662                      QUIKBAS Subboard
 From:  STEVE DEMO                Sent: 06-12-93 21:09
   To:  EARL MONTGOMERY           Rcvd: -NO-
   Re:  BAISC CODE 1 OF 3

'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O

'>>> Start of page 1.

'Just a Quick Demo of ways to get areas of the Screen 13 into arrays
'and manipulate them. I know you can use get ect.. but I wanted to do
'it this way. These routines could be used in Loading Screens for Games
'although slow they are kinda neat. See ya Oh yes No Mickey this time.

DEFINT A-Z
'$DYNAMIC
DIM DoitA(1 TO 16000)  'first 1/4 of 1st screen
DIM Doitb(1 TO 16000)  'second 2/4 of 1st screen
DIM Doitc(1 TO 16000)  'third 3/4 of 1st screen
DIM Doitd(1 TO 16000)  'forth 4/4 of 1st screen

DIM aDoitA(1 TO 16000)  'first 1/4 of 2nd screen
DIM aDoitb(1 TO 16000)  'second 2/4 of 2nd screen
DIM aDoitc(1 TO 16000)  'third 3/4 of 2nd screen
DIM aDoitD(1 TO 16000)  'forth 4/4 of 2nd screen
CONST PI = 3.141593
SCREEN 0
WIDTH 40
RANDOMIZE TIMER
COLOR 31
LOCATE 12, 5: PRINT "Ok another stupid Graphic Demo": SLEEP 3
SCREEN 13
'Lets Make some pretty pictures
PixleColor = 79
FOR x = 0 TO 199
  PixleColor = PixleColor + 1
  IF PixleColor > 100 THEN PixleColor = 79
FOR xxx = 0 TO 319
    PSET (xxx, x), PixleColor
   NEXT xxx
NEXT x
FOR a = 1 TO 30
 Xcord = RND * 320
 ycord = RND * 200
 Coulors = INT(50 * RND) + 1
 LINE (Xcord, ycord)-(INT(300 * RND), INT(200 * RND)), Coulors, B
NEXT
FOR a = 1 TO 100
 Xcord = RND * 320
 ycord = RND * 200
 Coulors = INT(150 * RND) + 1
 CIRCLE (Xcord, ycord), INT(10 * RND) + 1, Coulors, -PI, -PI / 2
 PAINT (Xcord + 1, ycord), INT(100 * RND) + 1, Coulors
NEXT
D = 0       ' Now lets save the first screen in a array
FOR x = 0 TO 49
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = POINT(xxx, x): DoitA(D) = PixClr
    PixClr = POINT(xxx, x + 50): Doitb(D) = PixClr
    PixClr = POINT(xxx, x + 100): Doitc(D) = PixClr
    PixClr = POINT(xxx, x + 150): Doitd(D) = PixClr
   NEXT xxx
NEXT x
CLS   ' Lets Draw The Next Screen
FOR a = 1 TO 30
 Xcord = RND * 320
 ycord = RND * 200
 Coulors = INT(50 * RND) + 1
 LINE (Xcord, ycord)-(INT(300 * RND), INT(200 * RND)), Coulors, B
NEXT
FOR a = 1 TO 100
 Xcord = RND * 320
 ycord = RND * 200
 Coulors = INT(150 * RND) + 1
 CIRCLE (Xcord, ycord), INT(40 * RND) + 1, Coulors, -PI, -PI / 2
 PAINT (Xcord + 1, ycord), INT(100 * RND) + 1, Coulors
NEXT
D = 0

FOR x = 0 TO 49                  ' Get Sections of the Display
' into Arrays
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = POINT(xxx, x): aDoitA(D) = PixClr
    PixClr = POINT(xxx, x + 50): aDoitb(D) = PixClr
    PixClr = POINT(xxx, x + 100): aDoitc(D) = PixClr
    PixClr = POINT(xxx, x + 150): aDoitD(D) = PixClr
   NEXT xxx
NEXT x
D = 0
'******** uncompress  arrays back into a picture
FOR times = 1 TO 2
D = 0
FOR x = 199 TO 150 STEP -1
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = DoitA(D): PSET (xxx, x), PixClr
   NEXT xxx
NEXT x
D = 0
FOR x = 149 TO 100 STEP -1
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = Doitb(D): PSET (xxx, x), PixClr
   NEXT xxx
NEXT x
D = 0
FOR x = 99 TO 50 STEP -1
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = Doitc(D): PSET (xxx, x), PixClr
    NEXT xxx
NEXT x
D = 0
FOR x = 49 TO 0 STEP -1
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = Doitd(D): PSET (xxx, x), PixClr
   NEXT xxx
NEXT x
D = 0
SOUND 400, 2
g = g + 1
IF g = 1 THEN
SCREEN 0: WIDTH 40: COLOR 31
CLS : LOCATE 10, 11: PRINT "Ain't Basic Fun ?": SLEEP 3: SCREEN 13
END IF
IF g = 2 THEN
SCREEN 0: WIDTH 40: COLOR 31
CLS : LOCATE 10, 11: PRINT "Cool Can I play 2": SLEEP 3: SCREEN 13
END IF
FOR x = 0 TO 49
  FOR xxx = 319 TO 0 STEP -1
    D = D + 1
    PixClr = aDoitA(D): PSET (xxx, x), PixClr
    PixClr = aDoitb(D): PSET (xxx, x + 50), PixClr
    PixClr = aDoitc(D): PSET (xxx, x + 100), PixClr
    PixClr = aDoitD(D): PSET (xxx, x + 150), PixClr
   NEXT xxx
NEXT x
D = 0
FOR x = 49 TO 0 STEP -1
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = DoitA(D): PSET (xxx, x), PixClr
    PixClr = Doitb(D): PSET (xxx, x + 50), PixClr
    PixClr = Doitc(D): PSET (xxx, x + 100), PixClr
    PixClr = Doitd(D): PSET (xxx, x + 150), PixClr
   NEXT xxx
NEXT x
D = 0
FOR x = 0 TO 49
  FOR xxx = 0 TO 319
    D = D + 1
    PixClr = aDoitA(D): PSET (xxx, x), PixClr
    PixClr = aDoitb(D): PSET (xxx, x + 50), PixClr
    PixClr = aDoitc(D): PSET (xxx, x + 100), PixClr
    PixClr = aDoitD(D): PSET (xxx, x + 150), PixClr

   NEXT xxx
NEXT x
NEXT times
PLAY "l35<ABC>"
ending:
a$ = INPUT$(1)
CLS
SCREEN 0
WIDTH 80, 25

'



Msg #:  6665                      QUIKBAS Subboard
 From:  STEVE DEMO                Sent: 06-13-93 00:53
   To:  ALL                       Rcvd: -NO-
   Re:  EGA WINDOWS 1 OF 4

'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O

'>>> Start of page 1.

'I am working on a QWK reader could someone post some code
'on Reading and Writeing .REP packets ?
'These are the Window Routines I have come up with let me
'know what ya think. I'm useing them in my Reader Oh yeah it's EGA
'These Routines Are FREE to anyone who wants to Mangle them.
'I have included a Short Demo on how to call them. Have Fun
'Written By -----> Steve Demo
DEFINT A-Z
'$INCLUDE: 'qb.bi'
DECLARE SUB Intro ()
DECLARE SUB Clocks ()
DECLARE SUB Pause (ticks%)
DECLARE SUB NewClear (Clur)
DECLARE SUB BackDrop (Clur)
DECLARE SUB box (x, y, xx, yy, Clur)
DECLARE SUB BoxFill (x, y, xx, yy, Clur)
DECLARE SUB GetColor (Clur, clur1, clur2)
DECLARE SUB ClacArray9 (num!, x, y, xx, yy) 'used for get and put
DECLARE SUB Rim (x, y, xx, yy, Clur, InOut) 'Notice that Rim
' Dosen't place the
    'Rim where you might think it is
    'offset by 2 to match up with the
    'Button Routine 1 for in else out
DECLARE SUB Button (x, y, xx, yy, Clour, InOut) 'declare the
' Inout as 1 for
'in and anything else for
'an out Button
DECLARE SUB ColorPrint (TEXT$, ROW%, COL%, FC%, BC%) 'Thanks to
' who ever
     'posted this routine
     'It's Great


ON TIMER(60) GOSUB Clock
SCREEN 9
WIDTH , 43

Intro
Button 40, 20, 600, 320, 7, 0
Button 45, 25, 595, 315, 7, 1
Button 50, 30, 590, 55, 7, 0
Button 55, 35, 585, 50, 7, 1
ColorPrint "File  Display    VGA    EGA   DEMO", 6, 10, 4, 7
Pause 18
Rim 300, 35, 360, 50, 7, 0
SOUND 100, 1: Pause 18
Rim 300, 35, 360, 50, 7, 1
SOUND 50, 1: Pause 18: NewClear 0

BoxFill 0, 0, 639, 349, 7
Button 3, 3, 632, 347, 7, 1
Button 14, 55, 620, 336, 7, 0
Button 14, 8, 480, 50, 7, 0
Button 18, 12, 476, 46, 7, 1
Button 25, 65, 605, 330, 7, 1
Button 35, 75, 595, 320, 1, 1
ColorPrint "EXIT   CONTINUE", 4, 5, 14, 7
Rim 25, 18, 70, 37, 7, 1
'draw clock body ***************
Button 490, 10, 602, 47, 7, 0'*
Button 499, 17, 593, 40, 7, 0'*
Rim 502, 20, 590, 37, 7, 1    '*
Clocks                        '*
'display first clock ***********
TIMER ON
Rim 80, 18, 160, 37, 7, 1
Pause 18
Rim 80, 18, 160, 37, 7, 0
SOUND 100, 1: Pause 18
Rim 80, 18, 160, 37, 7, 1
SOUND 50, 1: Pause 18

TIMER OFF

BackDrop 15

Button 0, 0, 639, 349, 7, 0
Button 10, 40, 630, 345, 15, 0
Button 0, 0, 30, 20, 7, 0
Button 4, 5, 26, 15, 7, 0
Button 600, 0, 639, 20, 7, 0
LINE (619, 4)-(619, 18), 8
BoxFill 30, 0, 599, 20, 1
BoxFill 0, 20, 639, 35, 15

ColorPrint "BASIC WINDOWS v 1.00 Steve Demo", 2, 27, 15, 1
ColorPrint CHR$(31), 2, 77, 8, 7
ColorPrint CHR$(30), 2, 79, 8, 7
ColorPrint "EXIT   File   Copy   Borrow   Keep   QB   Lives ", 4, 3, 8, 15
Pause 35
FOR x = 1 TO 6
 ColorPrint "Ain't no C here Folks", 25, 30, 1, 15
 Pause 8
 ColorPrint STRING$(28, " "), 25, 30, 15, 15
 Pause 8
NEXT x
 ColorPrint "Quick BASIC LIVES !", 25, 30, 1, 15
 Pause 18
 ColorPrint "Take That Mickey Soft", 25, 30, 1, 15
 Pause 18
 ColorPrint STRING$(28, " "), 25, 30, 15, 15
Button 180, 180, 370, 210, 1, 0
 DO UNTIL LEN(INKEY$)
   Rim 180, 180, 370, 210, 1, 0
   ColorPrint "Press Any Key George", 25, 25, 15, 1
   SOUND 300, 1: Pause 9
   ColorPrint "Press Any Key George", 25, 25, 7, 1
   Rim 180, 180, 370, 210, 1, 1
   SOUND 150, 1: Pause 9
 LOOP
Rim 180, 180, 370, 210, 1, 1
ColorPrint "Enter Your Code here", 25, 25, 12, 1
SOUND 200, 1: SOUND 300, 1: SOUND 400, 1: Pause 18
NewClear 0
Pause 5
FOR x = 14 TO 9 STEP -1    'this is what you call OVER KILL
 BackDrop x                'I couldn't resist
 NewClear 0
 BackDrop x
NEXT x
Pause 5
NewClear 0
SCREEN 0
WIDTH , 25: COLOR 15
Pause 2  'couldn't remember how to call the wait cmd so I used
' this
 'my machine displays the Print cmd before the width gets
 'finished switcing the screen
LOCATE 14, 30: PRINT "So I'm a Ham"
END
Clock:
Clocks
SOUND 400, .1
RETURN

SUB BackDrop (Clur)
 x = 639
 FOR y = 149 TO 0 STEP -1
  x = x - 5
  box 0 + x, 0 + y, 639 - x, 349 - y, Clur
 NEXT y
END SUB

SUB box (x, y, xx, yy, Clur)
LINE (x, y)-(xx, yy), Clur, B
END SUB

SUB BoxFill (x, y, xx, yy, Clur)
LINE (x, y)-(xx, yy), Clur, BF
END SUB

SUB Button (x, y, xx, yy, Clour, InOut)
GetColor Clour, Clour1, Clour2
IF InOut = 1 THEN
 LINE (x, y)-(xx, yy), Clour, BF
 LINE (x + 2, y + 2)-(xx - 2, yy - 2), Clour1, B
 LINE (x + 2, y + 2)-(x + 2, yy - 2), Clour2
 LINE (x + 2, y + 2)-(xx - 2, y + 2), Clour2

ELSE
 LINE (x, y)-(xx, yy), Clour, BF
 LINE (x + 2, y + 2)-(xx - 2, yy - 2), Clour2, B
 LINE (x + 2, y + 2)-(x + 2, yy - 2), Clour1
 LINE (x + 2, y + 2)-(xx - 2, y + 2), Clour1
END IF
END SUB

SUB ClacArray9 (num!, x, y, xx, yy)
num! = 4 + INT(((xx - x + 1) * (1) + 7) / 8) * 4 * ((yy - y) + 1)
IF num! > 32000 THEN : PRINT "You need 2 arrays for this"+_
" window": PRINT "press any key to end": a$ = INPUT$(1): END
END SUB

SUB Clocks
 GetTime$ = MID$(TIME$, 1, LEN(TIME$) - 3)
 Hour$ = MID$(GetTime$, 1, 2)
 Min$ = MID$(GetTime$, LEN(GetTime$) - 1, LEN(GetTime$))
 Hour = VAL(Hour$)
 IF Hour > 12 THEN
      AmPm$ = "PM"
      Hour = Hour - 12
      Hour$ = STR$(Hour)
 ELSE
 AmPm$ = "AM"
 END IF
 IF Hour = 0 THEN Hour$ = "12"
 NewTime$ = Hour$ + ":" + Min$ + " " + AmPm$
 ColorPrint NewTime$, 4, 65, 10, 7

 'You May Wish to leave this routine out It could scare someone
' ;-)
 chime$ = Hour$ + Min$
 IF LTRIM$(RTRIM$(chime$)) = "1200" THEN
  PLAY "l30t60<aaaBBBCCCBBBAAA<<aaaBBBCCCBBBAAA>>aaaBBBCCCBBBAAA"
 END IF
END SUB

SUB ColorPrint (TEXT$, ROW%, COL%, FC%, BC%)
  'Thanks to who ever posted this code I can't remember your name
  'but it works great so insert your name here _____________
  DIM inreg AS RegTypeX, outreg AS RegTypeX
  c$ = STRING$(LEN(TEXT$), 219)       ' String of solid chars
' for backgrnd
  inreg.ax = &H1300             ' Video service 13h, subfunction
' 0
  inreg.bx = BC%                ' Background colour
  inreg.cx = LEN(TEXT$)         ' String length
  inreg.dx = 256 * (ROW% - 1) + (COL% - 1)      ' Text pos. in
' "origin 0"
  inreg.es = VARSEG(c$)           ' String's segment
  inreg.bp = SADD(c$)           ' String's address
  CALL INTERRUPTX(&H10, inreg, outreg)     ' Output the
' background
  inreg.bx = (FC% XOR BC%) + &H80   ' BL=ForeColor; BH=&H80 uses
' XOR to draw
  inreg.es = VARSEG(TEXT$)
  inreg.bp = SADD(TEXT$)
  CALL INTERRUPTX(&H10, inreg, outreg) ' Output the text, XORing
' w/backgrnd

END SUB

SUB GetColor (Clour, Clour1, Clour2)
SELECT CASE Clour
  CASE 0: Clour1 = 7: Clour2 = 8
  CASE 1: Clour1 = 9: Clour2 = 8
  CASE 2: Clour1 = 10: Clour2 = 8
  CASE 3: Clour1 = 11: Clour2 = 8
  CASE 4: Clour1 = 12: Clour2 = 8
  CASE 5: Clour1 = 13: Clour2 = 8
  CASE 6: Clour1 = 7: Clour2 = 8
  CASE 7: Clour1 = 15: Clour2 = 8
  CASE 8: Clour1 = 15: Clour2 = 0
  CASE 9: Clour1 = 15: Clour2 = 1
  CASE 10: Clour1 = 15: Clour2 = 2
  CASE 11: Clour1 = 15: Clour2 = 3
  CASE 12: Clour1 = 15: Clour2 = 4
  CASE 13: Clour1 = 15: Clour2 = 5
  CASE 14: Clour1 = 15: Clour2 = 8
  CASE 15: Clour1 = 7: Clour2 = 8
  CASE ELSE
    BEEP: EXIT SUB
END SELECT
END SUB

SUB Intro
BackDrop 4
Button 220, 150, 420, 200, 5, 1
Rim 224, 154, 416, 196, 5, 0
ColorPrint "Basic  Windows", 21, 34, 7, 5
ColorPrint "By Steve Demo ", 23, 34, 7, 5
Pause 18
Rim 224, 154, 416, 196, 5, 1
Rim 220, 150, 420, 200, 5, 0
ColorPrint "Basic  Windows", 21, 34, 15, 5
ColorPrint "By Steve Demo ", 23, 34, 15, 5
Pause 22
END SUB

SUB NewClear (Clur)
 x = 639
 FOR y = 349 TO 0 STEP -1
  x = x - 5
  box 0 + x, 0 + y, 639 - x, 349 - y, Clur
 NEXT y
 CLS
END SUB

 SUB Pause (ticks%)
    DEF SEG = 0
    DO UNTIL TestTick% > ticks%
        LastTick% = GetTick%
        GetTick% = PEEK(&H46C)
         IF LastTick% <> GetTick% THEN
           TestTick% = TestTick% + 1
         END IF
    LOOP
    DEF SEG
 END SUB

SUB Rim (x, y, xx, yy, Clour, InOut)
GetColor Clour, Clour1, Clour2
IF InOut = 1 THEN
 LINE (x + 2, y + 2)-(xx - 2, yy - 2), Clour1, B
 LINE (x + 2, y + 2)-(x + 2, yy - 2), Clour2
 LINE (x + 2, y + 2)-(xx - 2, y + 2), Clour2
ELSE
 LINE (x + 2, y + 2)-(xx - 2, yy - 2), Clour2, B
 LINE (x + 2, y + 2)-(x + 2, yy - 2), Clour1
 LINE (x + 2, y + 2)-(xx - 2, y + 2), Clour1
END IF
END SUB
'


Msg #:  7122                      QUIKBAS Subboard
 From:  JIM LITTLE                Sent: 06-14-93 01:23
   To:  ERIC LOW                  Rcvd: -NO-
   Re:  (1/4) INPUT ROUTINE


'______O_/__________________| SNIP |__________________\_O______
'      O \                  | HERE |                  / O
'This file created by PostIt! v6.1.
'>>> Start of page 1.

'These routines will input a line of text of up 32K, within the bounds
' of the window specified.  If more text is inputted than there is room,
' the text scrolls.  Insert, delete, home and end all perform expected
' functions.  Color is not supported, but could be added without difficulty.
'A quirk: Although the text scrolls at 'right', an additional space is
' required for the cursor, and this space -will- overwrite anything at
' that location.  So count on allowing at least one blank space beyond
' 'right'.
'This routine works without speed problems on my 386DX/40.. but I have
' not tested on anything slower.  If anybody sees a problem, please let
' me know!

'Jim Little

'This code is not copyrighted.  It may be used by anyone for any purpose.

DECLARE SUB Printline (topletter AS INTEGER, text AS STRING,_
 left AS INTEGER, right AS INTEGER)
DECLARE SUB cInput (text AS STRING, left AS INTEGER, right AS_
 INTEGER, length AS INTEGER, flag AS INTEGER)
DECLARE SUB GetStroke (keystroke AS INTEGER)

CONST kBackspace = 8                   'ASCII values for some
' keys, as returned by GetStroke
CONST kTab = 9
CONST kReturn = 13
CONST kEscape = 27
CONST kSpace = 32
CONST kInsert = -82
CONST kDelete = -83
CONST kHome = -71
CONST kEnd = -79
CONST kPageUp = -73
CONST kPageDown = -81
CONST kUpArrow = -72
CONST kDownArrow = -80
CONST kLeftArrow = -75
CONST kRightArrow = -77

CONST cOk = 0                          'constants used by 'flag'
' in cInput
CONST cUpArrow = 1
CONST cDownArrow = 2
CONST cPageUp = 3
CONST cPageDown = 4
CONST cEscape = 5
CONST cNull = 6   'Note: not returned by cInput

CONST False = 0
CONST True = NOT False

'sample.. delete this and import remainder into your programs.

CLS
LOCATE , 32
PRINT "<-- Input scrolls at this point.";

text$ = "This is a test"
cInput text$, 1, 30, 80, flag%

PRINT : PRINT
PRINT "Text recieved: "; text$
PRINT
PRINT "Input terminated with ";
SELECT CASE flag%
   CASE cOk
      PRINT "a return."
   CASE cUpArrow
      PRINT "the up arrow."
   CASE cDownArrow
      PRINT "the down arrow."
   CASE cPageUp
      PRINT "a page up."
   CASE cPageDown
      PRINT "a page down."
   CASE cEscape
      PRINT "escape."
   CASE cNull
      PRINT "null.  (Wait.. that isn't possible!)"
END SELECT

SUB cInput (text AS STRING, left AS INTEGER, right AS INTEGER,_
 length AS INTEGER, flag AS INTEGER)
'Controlled input of text.  Inputs string of text on current line, starting at
' left and continuing to right.  If length is longer than space allows, text
' scrolls to left.
'Flag is set to Cescape, CupArrow, CdownArrow, CpageUp, CpageDown, or Cok ' depending on what
' key the user used to terminate input.  Cok signifies normal (return)
' termination.

DIM topletter AS INTEGER               'letter at left of window
DIM curletter AS INTEGER               'letter at cursor position
DIM finished AS INTEGER                'true if user finished typing line
DIM keystroke AS INTEGER               'user's last keystroke
DIM tabsp AS INTEGER                   'number of spaces to tab when Tab pressed
STATIC notinsert AS INTEGER            'false if insert is on,  true otherwise

text = RTRIM$(text)        'trim off all extra spaces
topletter = 1
curletter = 1
finished = False
Printline 1, text, left, right

'following in case cursor size changes between calls
IF NOT notinsert THEN
   LOCATE , , , 4, 5  'change cursor size to large block
ELSE
   LOCATE , , , 0, 5    'change cursor size to thin line
END IF
DO
   LOCATE , left + curletter - topletter, 1
   GetStroke keystroke
   LOCATE , , 0
   SELECT CASE keystroke
   CASE kInsert
      notinsert = NOT notinsert
      IF NOT notinsert THEN
         LOCATE , , , 4, 5  'change cursor size to thin line
      ELSE
         LOCATE , , , 0, 5    'change cursor size to large block
      END IF
   CASE kDelete
      IF LEN(text) >= 1 AND curletter <> LEN(text) + 1 THEN
         MID$(text, curletter) = MID$(text, curletter + 1)
         text = LEFT$(text, LEN(text) - 1)
         Printline topletter, text, left, right
      END IF
   CASE kBackspace
      IF curletter > 1 THEN
         text = LEFT$(text, curletter - 2) + RIGHT$(text,_
 LEN(text) - curletter + 1)
         curletter = curletter - 1
         IF curletter < topletter THEN
            topletter = topletter - 1
         END IF
         Printline topletter, text, left, right
      END IF
   CASE kHome
      IF curletter > 1 THEN
         curletter = 1
         IF curletter < topletter THEN
            topletter = 1
         Printline topletter, text, left, right
         END IF
      END IF
   CASE kEnd
      IF curletter < LEN(text) + 1 THEN
         curletter = LEN(text) + 1
         IF curletter > topletter + right - left THEN
            topletter = LEN(text) - right + left + 1
            Printline topletter, text, left, right
         END IF
      END IF
   CASE kLeftArrow
      IF curletter > 1 THEN
         curletter = curletter - 1
         IF curletter < topletter THEN
            topletter = topletter - 1
            Printline topletter, text, left, right
         END IF
      END IF
   CASE kRightArrow
      IF curletter < LEN(text) + 1 THEN
         curletter = curletter + 1
         IF curletter > topletter + right - left THEN
            topletter = topletter + 1
            Printline topletter, text, left, right
         END IF
      END IF
   CASE kPageUp
      flag = cPageUp
      finished = True
   CASE kPageDown
      flag = cPageDown
      finished = True
   CASE kUpArrow
      flag = cUpArrow
      finished = True
   CASE kDownArrow
      flag = cDownArrow
      finished = True
   CASE kEscape
      flag = cEscape
      finished = True
   CASE IS >= 32
      IF keystroke <= 127 AND NOT notinsert AND LEN(text) + 1 <= length THEN
      'valid character, with insert on
         text = LEFT$(text, curletter - 1) + CHR$(keystroke) + RIGHT$(text, LEN(text) - curletter + 1)
         curletter = curletter + 1
         IF curletter > topletter + right - left + 1 THEN
            topletter = topletter + 1
         END IF
         Printline topletter, text, left, right
      END IF
      IF keystroke <= 127 AND notinsert AND (curletter < LEN(text) + 1 OR LEN(text) + 1 <= length) THEN
      'valid character, with insert off
         IF curletter = LEN(text) + 1 THEN
            text = text + CHR$(keystroke)
         ELSE
            MID$(text, curletter, 1) = CHR$(keystroke)
         END IF
         curletter = curletter + 1
         IF curletter > topletter + right - left THEN
            topletter = topletter + 1
            Printline topletter, text, left, right
         ELSE
            PRINT CHR$(keystroke);
         END IF
      END IF
   CASE kTab
      IF length <> LEN(text) THEN
         IF LEN(text) + 3 <= length THEN
            tabsp = 3
         ELSE
            tabsp = length - LEN(text)
         END IF
         text = LEFT$(text, curletter - 1) + STRING$(tabsp, 32) + RIGHT$(text, LEN(text) - curletter + 1)
         curletter = curletter + tabsp
         IF curletter > topletter + right - left THEN
            topletter = topletter + tabsp
         END IF
         Printline topletter, text, left, right
      END IF
   CASE kReturn
      flag = cOk
      finished = True
   END SELECT

LOOP UNTIL finished

Printline 1, text, left, right

END SUB

SUB GetStroke (keystroke AS INTEGER)
'waits for then returns single character as integer.  Extended keystrokes
' returned as a negative.  (See CONST definitions).

DIM k AS STRING                        'key inputted

DO
   k = INKEY$
LOOP UNTIL LEN(k)
IF LEFT$(k, 1) = CHR$(0) THEN
   keystroke = ASC(MID$(k, 2)) * -1
ELSE
   keystroke = ASC(k)
END IF

END SUB

DEFINT A-Z
SUB Printline (topletter AS INTEGER, text AS STRING, left AS_
 INTEGER, right AS INTEGER)
'prints a line of text, starting with topletter, within the bounds of
left and right

LOCATE , left
PRINT MID$(text, topletter, right - left + 1); SPC(right - POS(0) + 2);

END SUB

'




 From:  DAVE ARIGAN               Sent: 06-10-93 09:21
   To:  BENNETT HENDRY            Rcvd: -NO-
   Re:  (R)DIRS

 -=> Quoting Bennett Hendry to All <=-

 BH> Does anybody know of a good way to read directories from a disk
into a
 BH> variable? (like an array, perhaps?)  I want to write a recursive
 BH> routine to remove an entire directory branch, with full
 BH> sub-directories, but I can't get the directory names into a variable
 BH> in order to work with them.  ANY ideas would be appreciated.

The following reads a directory using Qbasic.  With some modifications,
you should have no problems adapting it to your program.  Remember,
use:

C:\QBASIC>qb /l lib\qb.qlb


DEFINT A-Z '$INCLUDE: 'QB.BI'

TYPE DataTransferArea
        Reserved1   AS STRING * 21
        Attribute   AS STRING * 1
        FileTime    AS INTEGER
        FileDate    AS INTEGER
        FileSize    AS LONG
        FIleName AS STRING * 13
END TYPE

TYPE DirectoryRecord
        FIleName    AS STRING * 13
        FileSize    AS LONG
        FileDate    AS INTEGER
        FileTime    AS INTEGER
        FileAttb    AS INTEGER
END TYPE

DIM SHARED InRegsX AS RegTypeX
DIM SHARED OutRegsX AS RegTypeX
DIM SHARED DTA AS DataTransferArea
DIM DirEntry AS DirectoryRecord

CLS
INPUT "Enter file specification: "; filespec$
CALL SetDTA(DTA)

FindStatus = FindFirst(0, filespec$, DirEntry)
CALL PrintDirEntry(DirEntry, FindStatus)
FindStatus = FindNext(DirEntry)

WHILE FindStatus = 0
        CALL PrintDirEntry(DirEntry, FindStatus)
        FindStatus = FindNext(DirEntry)
        CALL SetDTA(DTA)
WEND

END

FUNCTION FindFirst (Attr, FIleName$, DEntry AS DirectoryRecord)
        InRegsX.AX = &H4E00
        InRegsX.CX = Attr

        Spec$ = FIleName$ + CHR$(0)
        InRegsX.DS = VARSEG(Spec$) ' Load DS:DX with
        InRegsX.DX = SADD(Spec$)   ' address of Spec$
        CALL InterruptX(&H21, InRegsX, OutRegsX)

        FindFirst = OutRegsX.AX

        IF (OutRegsX.Flags AND 1) = 0 THEN
                CALL TransferDTA2DIR(DEntry)
                FindFirst = 0 'Clear error condition setting
        END IF
END FUNCTION

FUNCTION FindNext (DEntry AS DirectoryRecord)
        DTA.FIleName = SPACE$(13)
        InRegsX.AX = &H4F00
        CALL InterruptX(&H21, InRegsX, OutRegsX)
        FindNext = OutRegsX.AX
        IF (OutRegsX.Flags AND 1) = 0 THEN
                CALL TransferDTA2DIR(DEntry)
                FindNext = 0
        END IF
END FUNCTION

FUNCTION FmtDate$ (FDate)
        Day = FDate AND &H1F
        Month = (FDate AND &H1E0) \ 32
        Year = (FDate AND &HFE00) \ 512 + 1980
        FmtDate$ = RStr$(Month, 2) + "-" + RStr$(Day, 2) + "-" + RStr$(Year, 4)
END FUNCTION

FUNCTION FmtTime$ (T%)
        Seconds = (T% AND &H1F) * 2
        Minutes = (T% AND &H7E0) \ 32

        Hours = (T% < 0) * (-16) + ((T% AND &H7FFF) \ 2048)
        Abbr$ = " am"
        IF Hours = 12 THEN Abbr$ = " pm"
        IF Hours = 0 THEN Hours = 12

        IF Hours > 12 THEN
                Hours = Hours MOD 12
                Abbr$ = " pm"
        END IF
        FmtTime$ = RStr$(Hours, 2) + ":" + RStr$(Minutes, 2) + ":" + RStr$(Seconds, 2)
END FUNCTION

SUB PrintDirEntry (DR AS DirectoryRecord, FindStatus)
        FmtStr$ = "\          \  ##,###,###  " + "\        \ \           \ ###"
        IF FindStatus = 0 THEN
                PRINT USING FmtStr$; DR.FIleName; DR.FileSize;
                   FmtDate$(DR.FileDate); FmtTime
        ELSE
                PRINT "Error on file lookup"
                SELECT CASE FindStatus
                        CASE 2 PRINT "File not found"
                        CASE 3 PRINT "Path not found"
                        CASE 18 PRINT "Match not found"
                        CASE ELSE PRINT "Unknown error #"; FindStatus
                END SELECT
        END IF
END SUB

FUNCTION RStr$ (X%, LX%)
        X$ = STR$(X%)
        RStr$ = RIGHT$("00000" + RIGHT$(X$, LEN(X$) - 1), LX%)
END FUNCTION

SUB SetDTA (DTA AS DataTransferArea)
        InRegsX.AX = &H1A00
        InRegsX.DS = VARSEG(DTA)
        InRegsX.DX = VARPTR(DTA)
        CALL InterruptX(&H21, InRegsX, OutRegsX)
END SUB

SUB TransferDTA2DIR (DEntry AS DirectoryRecord)
        DEntry.FIleName = DTA.FIleName
        DEntry.FileSize = DTA.FileSize
        DEntry.FileDate = DTA.FileDate
        DEntry.FileTime = DTA.FileTime
        DEntry.FileAttb = ASC(DTA.Attribute)
END SUB

' Pcode V1.0b - written by David Arigan
'
' Features: 16 bit CRCs
'           Fast 7 bit encryption
'           File Date/Time preservation
'           Ignores extra line spacing and/or garbage
'
' Usage:    QB /RUN PCODE.BAS /L LIB\QB.QLB
'
' $INCLUDE: 'qb.bi'

DECLARE SUB parsename (file$, ext$)
DECLARE SUB decode ()
DECLARE SUB decodeline ()
DECLARE SUB settimedate (file$, time&, date&)
DECLARE SUB gettimedate (file$, time&, date&)
DECLARE SUB crc16 (byte%)
DECLARE SUB encodeblock ()
DECLARE SUB send (flag%)
DECLARE SUB encode ()
DECLARE SUB closeh (handle%)
DECLARE FUNCTION openh% (file$)
DECLARE FUNCTION dec& (hexnum$)
DECLARE SUB fileerror (errnum%)

DEFINT A-Z

DIM SHARED buffer AS STRING
DIM SHARED bsegment AS INTEGER
DIM SHARED boffset AS INTEGER
DIM SHARED crctt AS LONG
DIM SHARED length AS LONG
DIM SHARED destlen AS LONG
DIM SHARED lines AS INTEGER
DIM SHARED block AS INTEGER
DIM SHARED inreg AS RegTypeX
DIM SHARED outreg AS RegTypeX
DIM SHARED mscode AS INTEGER
DIM SHARED lscode(0 TO 3)  AS INTEGER
DIM SHARED power AS INTEGER
DIM SHARED cpos AS INTEGER
DIM SHARED line$, infile$, outfile$

CLS
PRINT "PCode V1.0 - written by David Arigan"
PRINT
PRINT "1) Encode file"
PRINT "2) Decode file"
PRINT "3) Quit"
PRINT
PRINT "Choice: "; : LOCATE , , 1
DO: a$ = INKEY$: LOOP UNTIL a$ = "1" OR a$ = "2" OR a$ = "3"
PRINT a$
PRINT : LOCATE , , 0
IF a$ = "3" THEN CLS : END
LINE INPUT "Source Filename: "; infile$
IF infile$ = "" THEN RUN
PRINT
IF a$ = "1" THEN OPEN infile$ FOR BINARY AS #1
IF a$ = "2" THEN OPEN infile$ FOR INPUT AS #1
length = LOF(1): IF length = 0 THEN CALL fileerror(2)
IF a$ = "1" THEN CALL encode
IF a$ = "2" THEN CALL decode
PRINT "Total lines:"; lines
PRINT "Source file length:"; length
PRINT "Destination file length"; destlen
PRINT "Ratio: "; LTRIM$(STR$(destlen * 100 \ length)); "%"
END

SUB closeh (handle)
        inreg.ax = &H3E00
        inreg.bx = handle
        CALL INTERRUPTX(&H21, inreg, outreg)
        IF outreg.flags AND 1 THEN fileerror (6)
END SUB

SUB crc16 (byte)
        crctt = (crctt XOR byte * 256&) * 2
        IF crctt AND 32768 THEN crctt = crctt XOR 4129
        crctt = crctt * 2 AND 65535
END SUB

FUNCTION dec& (hexnum$)
        FOR i = 1 TO LEN(hexnum$)
                hexdigit = ASC(MID$(hexnum$, i, 1))
                decnum& = decnum& * 16 + hexdigit - 48 + 7 * (hexdigit> 64)
        NEXT i
        dec& = decnum&
END FUNCTION

SUB decode
decode1:
        INPUT #1, header$: version$ = LEFT$(header$, 7)
        IF version$ <> "pcode11" AND version$ <> "pcode12" THEN
                IF EOF(1) THEN CALL fileerror(3) ELSE GOTO decode1
        END IF
        IF version$ = "pcode11" THEN ll = 280 ELSE ll = 260
        length = dec&(MID$(header$, 8, 7))
        crcorg& = dec&(MID$(header$, 15, 4))
        ptime& = dec&(MID$(header$, 19, 4))
        pdate& = dec&(MID$(header$, 23, 4))
        outfile$ = RTRIM$(MID$(header$, 27, 8))
        outfile$ = outfile$ + "." + RTRIM$(MID$(header$, 35, 3))
        OPEN outfile$ FOR OUTPUT AS #2 LEN = 4096
        lines = length * 5 \ ll + 1
        FOR a = 1 TO lines
decode2:
                LINE INPUT #1, buffer: buffer = RTRIM$(buffer)
                IF LEFT$(buffer, 2) <> "dA" THEN
                        IF EOF(1) THEN CALL fileerror(7) ELSE GOTO decode2
                END IF
                CALL decodeline
        NEXT a
        destlen = LOF(2): length = LOF(1)
        CLOSE #1, #2
        CALL settimedate(outfile$, ptime&, pdate&)
        IF crcorg& <> crctt THEN CALL fileerror(1)
END SUB

SUB decodeline
        a& = SADD(buffer): a& = a& - 65536 * (a& < 0)
        bsegment = VARSEG(buffer) + (a& \ 16): boffset = (a& MOD 16)
        DEF SEG = bsegment
        FOR a = 2 TO LEN(buffer) - 1
                code = PEEK(boffset + a) - 35
                cpos = cpos - 1
                IF cpos = -1 THEN
                        cpos = 4: mscode = code
                ELSE
                        byte = code + (mscode MOD 3) * 92
                        mscode = mscode \ 3
                        PRINT #2, CHR$(byte);
                        CALL crc16(byte)
                END IF
        NEXT a
END SUB

SUB encode
        count& = length: block = 4096: power = 1: y = CSRLIN
        line$ = SPACE$(65): buffer = SPACE$(4096)
        outfile$ = infile$: CALL parsename(outfile$, ext$)
        OPEN outfile$ + ".pcd" FOR OUTPUT AS #2 LEN = 4096
        PRINT #2, "pcode12"; RIGHT$("000000" + HEX$(length), 7);
        PRINT #2, "000000000000"; LEFT$(outfile$ + "        ", 8);
        PRINT #2, LEFT$(ext$ + "   ", 3)
        WHILE (count&)
                IF count& < block THEN block = count&: buffer = SPACE$(block)
                GET #1, , buffer
                CALL encodeblock
                count& = count& - block
                LOCATE , 1: PRINT "Bytes Left:"; STR$(count&); "   ";
        WEND
        CALL send(1)
        CLOSE #1
        CALL gettimedate(infile$, ptime&, pdate&)
        SEEK #2, 15: PRINT #2, RIGHT$("000" + HEX$(crctt), 4);
        PRINT #2, RIGHT$("000" + HEX$(ptime&), 4);
        PRINT #2, RIGHT$("000" + HEX$(pdate&), 4);
        destlen = LOF(2)
        CLOSE #2
        PRINT
END SUB

SUB encodeblock
        a& = SADD(buffer): a& = a& - 65536 * (a& < 0)
        bsegment = VARSEG(buffer) + (a& \ 16): boffset = (a& MOD 16)
        DEF SEG = bsegment
        FOR pointer = 0 TO block - 1
                byte = PEEK(boffset + pointer)
                CALL crc16(byte)
                lscode(cpos) = byte MOD 92
                mscode = mscode + (byte \ 92) * power
                power = power * 3
                cpos = cpos + 1
                IF cpos = 4 THEN
                        CALL send(0)
                        power = 1
                        cpos = 0
                        mscode = 0
                END IF
        NEXT pointer
END SUB

SUB fileerror (errornum)
        CLS : PRINT "ERROR: ";
        IF errornum = 1 THEN PRINT "Bad CRC, file could be corrupt."
        IF errornum = 2 THEN PRINT "Source file not found."
        IF errornum = 3 THEN PRINT "Incorrect version."
        IF errornum = 4 THEN PRINT "Can't read file time/date."
        IF errornum = 5 THEN PRINT "Can't write file time/date."
        IF errornum = 6 THEN PRINT "Can't access file for I/O."
        IF errornum = 7 THEN PRINT "Source file too short."
        END
END SUB

SUB gettimedate (file$, time&, date&)
        handle = openh(file$)
        inreg.ax = &H5700
        inreg.bx = handle
        CALL INTERRUPTX(&H21, inreg, outreg)
        time& = outreg.cx
        date& = outreg.dx
        IF outreg.flags AND 1 THEN CALL fileerror(4)
        CALL closeh(handle)
END SUB

FUNCTION openh (file$)
        f$ = file$ + CHR$(0)
        inreg.dx = SADD(f$)
        inreg.ds = VARSEG(f$)
        inreg.ax = &H3D02
        CALL INTERRUPTX(&H21, inreg, outreg)
        IF outreg.flags AND 1 THEN CALL fileerror(6)
        openh = outreg.ax
END FUNCTION

SUB parsename (file$, ext$)
        ext$ = ""
        FOR a = LEN(file$) TO 1 STEP -1
                IF INSTR(":\", MID$(file$, a, 1)) THEN
                        file$ = MID$(file$, a + 1)
                        EXIT FOR
                END IF
        NEXT a
        FOR a = LEN(file$) TO 1 STEP -1
                IF MID$(file$, a, 1) = "." THEN
                        ext$ = MID$(file$, a + 1)
                        file$ = LEFT$(file$, a - 1)
                        EXIT FOR
                END IF
        NEXT a
END SUB

SUB send (flag) STATIC
        IF NOT flag THEN
                lnpos = lnpos + 1
                MID$(line$, lnpos) = CHR$(mscode + 35)
                FOR a = 1 TO cpos
                    MID$(line$, lnpos + a) = CHR$(lscode(a - 1) + 35)
                NEXT a
                lnpos = lnpos + 4
        END IF
        IF lnpos = 65 OR flag THEN
                lnpos = 0: PRINT #2, "dA"; RTRIM$(line$)
                line$ = SPACE$(65)
                lines = lines + 1
        END IF
END SUB

SUB settimedate (file$, time&, date&)
        handle = openh(file$)
        inreg.ax = &H5701
        inreg.bx = handle
        inreg.cx = time&
        inreg.dx = date&
        CALL INTERRUPTX(&H21, inreg, outreg)
        IF outreg.flags AND 1 THEN CALL fileerror(5)
        CALL closeh(handle)
END SUB

'