MCOMM 6.00 UPDATE NOTES

         Added support for IRQs 8-15 and improved the documentation
         on how to find the values for the IRQ masks and vector
         numbers.  Corrected an oversight in async_restart that
         caused it to not work on some ports when 3 or more ports
         were open simultaneously.

         Note: The 6.00 version designation (versus 5.60) is because
         I use the timestamp on the files to indicate what version of
         MCOMM they belong to.  Since a file can't be timestamped
         as 5:60, I had to change the major number.


                             MCOMM 5.59 UPDATE NOTES

         Forgot a switch when compiling version 5.58 which caused
         Microsoft's default library names to be embedded in the OBJs.
         The result is you had to tell your linker to ignore default
         library specs, rename a lib to be called xLIBCE, or (if
         you didn't know what to do) stay with version 5.57.  5.59
         does not reference any default libraries.  Other changes:
         Under certain conditions async_open did not restore interrupt
         vectors properly if the open failed.  This is corrected.
         Documented some additional v_scrlm mode options that were
         added to make it easier to extend the video routines to
         support VT100 emulation (see SUPLMNT.DOC).  Added some code
         to the TXZM.C port open routine to overcome a serial port
         lock up problem with some early PCI motherboards (you may
         want to steal this and put it in your open loop--a lot of
         PCs are affected).


                             MCOMM 5.58 UPDATE NOTES

         The version 5.58 update consists only of changes to the TXZM
         source code.  See TXZM.DOC for the list of updates.



                             MCOMM 5.57 UPDATE NOTES

         Made a change to an internal routine that initiated transmit
         interrupts.  This change fixes 2 problems--one with some new
         UARTs that recently appeared, and the other with failed or very
         slow transmits when running a program that uses MCOMM in a DOS
         box under OS/2.

         The COMM.H header file was modified to include vector numbers
         and IRQ masks for IRQs other than 3 and 4.

         Fixed a problem with the RecurseSubdirs function in TXZM.C.  It
         sometimes lost track of the current directory if the recurse
         subdirectories option was used when sending files.

         Registered users of 5.50+ may download a free upgrade to 5.57
         by logging onto N.E.T. Datalink, 903-838-6713, and leaving a
         message to the sysop that includes:

             1) Registration number from the original disk.
             2) Whether the original registration was for "Source
                and Libraries" or "Libraries Only".
             3) Your name and address.  This must match the name and
                address the software was originally registered under
                unless you have moved.

        Please allow 3 or 4 days from the time you leave the message
        requesting the update until you call back to download it.

        Mail in updates are $10.  See ORDER.DOC if you want a mail in
        update.

                           MCOMM 5.54-5.56 UPDATE NOTES

         Up to four ports may now be opened simultaneously as long as
         they do not share port addresses, IRQ lines, or vector numbers.
         Previously the limit was 2 simultaneous ports.  The AT extended
         IRQ lines (IRQs 8 thru 15) are not supported.

         A new use for 'v_scrlm' flag in the ANSI video code has been
         implemented making it easier to develop code that emulates the
         VT100.  Setting 'v_scrlm' to -1 causes the screen and cursor
         positioning to behave properly for VT100 no scroll mode.  This
         change should have no effect on existing code.

         Fixed a bug in the video code that occurred when a backspace
         character was displayed within a string with direct writes
         enabled.  (This last change is the difference between 5.55 and
         the 5.54 beta).  Version 5.56 consisted of a change to TXZM.C
         demo to account for change in COMM_S.LIB noted in following
         paragraph.



VERY IMPORTANT:

         If your code uses the option to disable or ignore the 16550
         FIFOs, or if your code disables MSR or LSR interrupts, you must
         make some changes to your source before using the new libs.  In
         order to support port addresses above 0x0FFFh, it was necessary
         to not use the high bits of the async_open ComBase parameter as
         flags.  Flags affecting 16550 operation and LSR/MSR interrupts
         must now be OR'd with the 'vctrnbr' argument of async_open
         rather than the 'combase' parameter.  ASYNC.DOC reflects these
         changes to the async_open function.



                             MCOMM 5.52 UPDATE NOTES

         No changes have been made to the serial code.  The video
         code includes a new feature that allows installing your own
         handler for unrecognized ANSI sequences (see SUPLMNT.DOC).
         The demos were updated to work with the latest versions of
         Borland/Turbo C/C++ and Microsoft C/C++.  The latest version
         of Zortech C/C++ the code has been tested with is 2.00.  They
         should work with later versions of ZTC with few or no changes.

         The ZMODEM demo (TXZM) was organized a little differently so
         all three supported compilers could use the the same ZMLIBs,
         rather than having a set of ZMLIBs for each memory model for
         each compiler.  This required including another module of the
         source code in the shareware version of MCOMM (XYZGEN.C) that
         formerly only came with the registered version.  This change
         also fixed some linker "unresolved external" errors for users
         of earlier versions of Turbo C.

         The TXZM demo now will respond with a CPR (cursor position
         report) sequence when it is sent an ANSI DSR (device status
         request).  This is so BBS systems that auto-detect ANSI will
         recognize TXZM's mini-terminal mode as an ANSI capable program.
         The implementation of this feature in TXZM is also a good
         example of how to put an unrecognized ANSI sequence handler in
         your program if you are using the MCOMM video functions.

         Support for "Doorway" mode was added to TXZM.  Pressing ALT=
         while in mini-terminal mode toggles this mode on and off.  The
         screen switches to a 25 line display when Doorway mode is on
         and reverts back to a 24 line display when Doorway mode is off.
         Since the purpose of Doorway mode is to allow the sending of
         special keys such as function keys, the arrow keys, PGUP, PDDN,
         etc., none of the TXZM program functions (including Exit, Help,
         Shell, etc.) work while Doorway mode is enabled.

         An otherwise undocumented -7 switch was added to TXZM.  This
         switch strips the high bit from incoming characters when in
         mini-terminal mode.





                             MCOMM 5.50 UPDATE NOTES

         Version 5.50 adds RTS flow control for the receive side.
         Previous versions supported monitoring CTS to insure the device
         being sent to was not overran but did not lower RTS if the PC
         was being overran.  The function 'async_msrflow' has been
         modified to support this option.  For more information, see the
         updated documentation on 'async_msrflow' in ASYNC.DOC.  This
         change also necessitated a change in the ASYNC structure making
         it one byte longer.  BE SURE TO USE THE RIGHT HEADER FILE AND
         RECOMPILE ANY CODE THAT USES COMM.H or COMM.HPP.

         Added a Zmodem demo program called TXZM.  The shell code and
         linkable libraries are not part of the shareware version of
         MCOMM.  Complete source comes with the registered version.
         This is primarily a demo with limited documentation and limited
         support.  It also happens to be very fast and contains a lot of
         extras.  It MAY NOT be distributed except as stated in its
         documentation.


                             MCOMM 5.41 UPDATE NOTES

         Version 5.41 contains a few minor changes and bug fixes.  These
         are:

         1) The 'volatile' keyword was added to ASYNC structure members
            that are modified by the interrupt handler.  This corrects
            problems with optimizing compilers (such as MSC 6.0) that
            load variables into registers.  Many of the macro
            implemented functions test variables that are modified by
            the interrupt handler.  If the compiler, in optimizing a
            loop, loads a variable into a register that is modified by
            the interrupt handler, it will never see the variable
            change.  The 'volatile' key word instructs the compiler to
            not assume the variable remains constant.  Thanks to Chris
            Fanning for pointing this out to me.

         2) The ANSI cursor position sequence did not recognize the
            window relative ('v_wrel') mode of operation.  If an ANSI
            cursor sequence was received, it was always treated relative
            to 0,0.  It now treats the current window's top left corner
            as 0,0 if 'v_wrel' is non-zero.  Thanks to David Speer for
            this information.

         3) When a line was exactly the width of the screen, any
            following CR/LFs were ignored until a non CR/LF character
            was received.  This is now fixed.

         4) The definition of SHFT_TAB in KEYS.H has been wrong for the
            last several versions.  Thanks to Cleo Yarber for pointing
            this out to me several times.





                             MCOMM 5.40 UPDATE NOTES

         The 5.40 version of MCOMM corrects two problems:

         1) Some UARTs miss transmit interrupts when they are ran in
            full duplex mode.  Code was added to detect missed
            interrupts and correct the situation.  This condition would
            cause previous versions of MCOMM to quit transmitting until
            the transmit buffer was flushed or the port closed and
            reopened.  This bug only showed up when operating in full
            duplex mode and only with some UARTs.  Version 5.40 has been
            tested by running several megabytes of data through 8250,
            16450, and 16550 UARTs in full duplex mode and never fails
            to detect a missed interrupt and correct for it.

         2) The loop that loads bytes into the transmit FIFOs (or the
            transmit hold register if the UART isn't a 16550) updates
            the transmit buffer output pointer in a register.  The loop
            is in the transmit interrupt handler and in previous
            versions of MCOMM5 the transmit interrupt handler code was
            called by the routine that started up the transmitter.  If a
            transmit interrupt occurred while the transmit start up code
            was within this loop, the buffer output pointer could be
            corrupted.  The result was scrambled output.  This only
            happened if the transmitter was sent a character, allowed to
            empty, and then immediately sent another character.  If only
            one character was sent at a time slowly, as in typing, or if
            the buffer was loaded up rapidly as in a program loop,
            everything was OK.  If characters were sent in a program loop
            that put a "small" delay between characters (character
            pacing), it often failed.  This was corrected by changing
            the transmit initiate routine so that it toggles the
            transmit interrupt enable bit in the UART's interrupt enable
            register to initiate transmit interrupts rather than calling
            the interrupt handler directly.


         ADDITIONS:

         An option was added to the async_open function to force FIFO
         mode off.  Previously you could OR the ComBase parameter with
         0x8000 and the code skipped over the check for a 16550 UART.
         If it was there and on, it stayed on.  If it was there and off,
         it stayed off.  You can now OR the ComBase parameter with
         0x4000 to force the FIFOs to be off.  If you don't OR anything
         with the ComBase parameter the FIFOs will be enabled if a 16550
         is present.

         To deal with problems with the Western Digital 16550, the ASYNC
         port structure is now one element longer.  The new element is
         called 'IERVal'.  Also options were added to allow you to open
         a port without enabling MSR interrupts, LSR interrupts, or
         both.  See the notes on the WD16550 in ASYNC.DOC for more
         information.





         Conversion LIBs and a batch file were added to support Zortech
         C / C++.  C++ header files and a C++ demo program for either
         Turbo C++ or Zortech C++ were added.

         Two new macros are now defined in COMM.H.  They are:

         async_txcnt(ASYNC *port) -- returns number of bytes left
                                     in the transmit buffer still to
                                     be transmitted.  Use async_txempty
                                     if you are waiting for 0 byte
                                     condition -- it's more efficient.

         async_rxfree(ASYNC *port) - returns bytes of free space left
                                     in the receive buffer.


         VIDEO FUNCTIONS:

         One minor bug was fixed.  The rd_scrnd function returned an
         incorrect pointer if the function was called with a request to
         read 0 bytes.  The result string was correct but the return
         value was wrong.  It now returns the correct pointer.

         A new global variable was added to control whether a displayed
         backspace character was destructive or non-destructive.
         Previously it was always destructive and that still is the
         default.  The variable is v_bksp.  Setting v_bksp to 0 will
         cause the backspace character to be non-destructive.





                            MCOMM 5.20 UPGRADE NOTES

            Major changes in this version of MCOMM are support for the
         16550 UART's FIFO mode of operation, changes in the header
         files, new time-out functions, and updated documentation.


         16550 UART SUPPORT:

            The async code now supports the 16550 UART's FIFO mode of
            operation.  Key features are:

            1) The async_open function automatically detects a 16550 and
               enables its FIFOs (can be optionally defeated).

            2) Functions are provided to set the receiver FIFO trigger
               level and to control the maximum number of bytes to load
               into the transmit FIFO at one time.

            3) The interrupt handler has been re-written to make most
               efficient use of the FIFO registers (they process
               multiple bytes per interrupt).

            ASYNC.DOC contains full descriptions of the new functions
            and changes made to the old functions.  It also has some
            information on how to set the receiver FIFO trigger level
            and the 'maximum number of bytes to transmit to the FIFOs at
            one time' level to achieve the best results.


         HEADER FILE CHANGES:

            Due to stricter type checking of newer compilers, several
            functions that formerly were declared as taking 'char' argu-
            ments are now declared as taking 'int' arguments.  This
            prevents getting an excessive number of warnings when pass-
            ing constants to these functions.

            The 'cdecl' keyword was added to the function prototypes to
            prevent problems when compiling with Microsoft's 'fastcall'
            option enabled.  This keyword, as well as the 'near' and
            'far' keywords, may not be compatible with your compiler.
            See MUSTREAD.DOC for more information.

            All the video functions are now prototyped in ANSIDRV.H.
            Before half of them were in ANSIDRV.H and the rest were in
            EXTRA.H.


         TIME OUT FUNCTIONS:

            The time-out functions have been changed to a new version
            that takes a pointer to a 'long' rather than a pointer to a
            TIMEOUT structure.  The new functions are faster and work
            with longer timeouts than the old versions.  Converting to
            the new style consists mainly of changing all occurrences of
            'struct TIMEOUT' in your code to 'long'.