V

                                   D

                                        S
            

                          VIRUS DETECTION SYSTEM

                         Professional Version 3.0


           Copyright (c) 1992-1994 by VDS Advanced Research Group
                            All Rights Reserved


                                September 1994
   

                                   WARNING
 
     THIS SOFTWARE AND MANUAL ARE BOTH PROTECTED BY U.S. COPYRIGHT LAW 
     (TITLE 17 UNITED STATES CODE). UNAUTHORIZED REPRODUCTION AND/OR SALES 
     MAY RESULT IN IMPRISONMENT OF UP TO ONE YEAR AND FINES OF UP TO
     $10,000 (17 USC 506). COPYRIGHT INFRINGERS MAY ALSO BE SUBJECT TO 
     CIVIL LIABILITY.

                                     
                                     DISCLAIMER

          The developers of VDS make no warranty of any kind, either express
     or implied, with respect to this software and accompanying documentation.
     In no event shall the developers be liable for any damages arising out 
     of the use of or inability to use the included programs. The entire risk 
     as to the results and performance of this software package is assumed by
     the customer. We specifically disclaim any implied warranties of 
     merchantability or fitness for any purpose. Use at your own risk.
          The developers of VDS reserve the right to revise the software and     
     accompanying documentation and to make changes in the contents without
     obligation to notify any person of such revision or changes.

                                  
                                  ACKNOWLEDGEMENTS

     We would like to thank a few people who helped us test and improve all 
     or parts of VDS. Specifically, Mike, Henri Delger, Paul Ferguson, 
     Vesselin Bontchev, Ahmed Yahya, Bill Whittington, Daniel Perez,
     and Bill Lambdin.

                                  
                                  TABLE OF CONTENTS

I. INTRODUCTION. . . . . . . . . . . . . . . . . . . . . . . . . . . . .  1
     A. Background . . . . . . . . . . . . . . . . . . . . . . . . . . .  1
          1. Do you need anti-viral programs?. . . . . . . . . . . . . .  1
          2. Will scanners protect me? . . . . . . . . . . . . . . . . .  1
          3. How is VDS different? . . . . . . . . . . . . . . . . . . .  1
     B. What is VDS? . . . . . . . . . . . . . . . . . . . . . . . . . .  1
     C. Why VDS. . . . . . . . . . . . . . . . . . . . . . . . . . . . .  2
     D. Components of VDS. . . . . . . . . . . . . . . . . . . . . . . .  3

II. SYSTEM REQUIREMENTS. . . . . . . . . . . . . . . . . . . . . . . . .  5
     A. Hardware & Software. . . . . . . . . . . . . . . . . . . . . . .  5

III. INSTALLATION. . . . . . . . . . . . . . . . . . . . . . . . . . . .  6
     A. INSTALL command line options . . . . . . . . . . . . . . . . . .  6
     B. Installing VDS . . . . . . . . . . . . . . . . . . . . . . . . .  6
          1. Express Setup:. . . . . . . . . . . . . . . . . . . . . . .  7
          2. Custom Setup: . . . . . . . . . . . . . . . . . . . . . . .  7
     C. Uninstalling VDS . . . . . . . . . . . . . . . . . . . . . . . .  8

IV. OPERATION of VDS . . . . . . . . . . . . . . . . . . . . . . . . . .  9
     A. Operational Cycle. . . . . . . . . . . . . . . . . . . . . . . .  9
     B. How does VDS work. . . . . . . . . . . . . . . . . . . . . . . .  9
          1. VDS command line options. . . . . . . . . . . . . . . . . . 11
          2. Configuration (VDSPRO30.INI) file . . . . . . . . . . . . . 12
     C. VDS as a scanner . . . . . . . . . . . . . . . . . . . . . . . . 14
          1. DUMPSIG and external virus signatures . . . . . . . . . . . 14
     D. VDS Device Driver. . . . . . . . . . . . . . . . . . . . . . . . 16
     E. VDSTSR . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 16
     F. VDSFSCAN . . . . . . . . . . . . . . . . . . . . . . . . . . . . 18
          1. Command line options. . . . . . . . . . . . . . . . . . . . 18
     G. VFSLITE. . . . . . . . . . . . . . . . . . . . . . . . . . . . . 19
          1. Options and default settings. . . . . . . . . . . . . . . . 19
          2. Configuration (VDSFSCAN.INI) file . . . . . . . . . . . . . 19
          3. Command line options. . . . . . . . . . . . . . . . . . . . 21
          4. DOS errorlevels returned. . . . . . . . . . . . . . . . . . 23
          5. Differences between VDSFSCAN and VFSLITE options. . . . . . 23
     H. How to use VITALFIX. . . . . . . . . . . . . . . . . . . . . . . 24
          1. Command line options. . . . . . . . . . . . . . . . . . . . 24
     I. Scenarios and Messages . . . . . . . . . . . . . . . . . . . . . 25
     J. Common Questions and Answers . . . . . . . . . . . . . . . . . . 26
     K. Known Problems and Conflicts . . . . . . . . . . . . . . . . . . 30

V. VIRUS ATTACK METHODS. . . . . . . . . . . . . . . . . . . . . . . . . 31
     A. Virus defined. . . . . . . . . . . . . . . . . . . . . . . . . . 31
     B. Features of PC Viruses . . . . . . . . . . . . . . . . . . . . . 31
          1. Stealth Virus . . . . . . . . . . . . . . . . . . . . . . . 31
          2. Dumb Virus. . . . . . . . . . . . . . . . . . . . . . . . . 31
          3. Encryptive Virus. . . . . . . . . . . . . . . . . . . . . . 31
          4. Polymorphic Virus . . . . . . . . . . . . . . . . . . . . . 31
     C. Types of PC Viruses. . . . . . . . . . . . . . . . . . . . . . . 32
          1. MBR/BR Virus. . . . . . . . . . . . . . . . . . . . . . . . 32
          2. Program Infector. . . . . . . . . . . . . . . . . . . . . . 32
               a. Simple Infector. . . . . . . . . . . . . . . . . . . . 32
               b. Companion Virus. . . . . . . . . . . . . . . . . . . . 32
               c. System Infector. . . . . . . . . . . . . . . . . . . . 32
          3. Multi-partite Virus . . . . . . . . . . . . . . . . . . . . 33
     D. Some facts about viruses . . . . . . . . . . . . . . . . . . . . 33

VI. PARTITION/BOOT SECTOR INFECTIONS . . . . . . . . . . . . . . . . . . 34
     A. Preliminary information. . . . . . . . . . . . . . . . . . . . . 34
     B. How to recover with RESTORE option . . . . . . . . . . . . . . . 37
     C. Manual Recovery Procedure. . . . . . . . . . . . . . . . . . . . 37

VII. HOW TO DEAL WITH VIRUSES. . . . . . . . . . . . . . . . . . . . . . 41
     A. Recommended Guidelines . . . . . . . . . . . . . . . . . . . . . 41



                         I. INTRODUCTION

A. Background

1. Do you need anti-viral programs?

    If someone had asked us this question five years ago, we would have 
probably said, "Yes, but if you're careful, only use diskettes from the 
factory, and don't use diskettes from other people, then you can probably 
get away without one." Unfortunately, the same is not true today. During the 
past few years we have seen an increase in the number of viruses from a few 
dozen to over 3000, and many of the new viruses are becoming more 
sophisticated. In addition, almost every major business that uses 
microcomputers has experienced a virus infection on some scale. Even some 
shrink-wrapped software from major software developers has been infected. 
It is just too much of a gamble not to have anti-virus protection these days. 

2. Will scanners protect me?

    While there are many anti-viral products on the market, the PC world has 
yet to see a comprehensive solution based on both scientific analysis and the
use of sophisticated techniques. A common feature shared by most anti-viral 
programs known as scanners is their pattern searching approach. They simply 
look for a sequence of identifying bytes (not necessarily consecutive) inside
existing executable code such as that contained in program files and boot 
sectors. This approach works quite well for many viruses. The trouble is that
a pattern searching approach requires fore-knowledge of specific viruses and
their identifiers. This means that they are useless against new, unknown 
viruses. In addition, new viruses which mutate upon each infection have been 
developed. They make extraction of an easily discernible search pattern 
impossible.

3. How is VDS different?

    VDS Advanced Research Group would like to shift the focus from simple 
pattern matching to one of analyzing viral behavior. In this way, rather 
than keeping the market alive through forcing users to upgrade frequently 
as others have done, we can instead offer a more comprehensive solution. 
If others had taken this approach, computer viruses may have been less of 
a threat than they certainly are today. You must remember that scanners
were first developed by well-meaning hackers who lacked a clear, long-term 
perspective in this matter. It was the most obvious and easiest thing to do 
at the time and  scanners became popular over time. 
    VDS (Virus Detection System) was developed in reaction to the limitations
of existing anti-viral programs. Due to the large number of ways that viruses
can exploit the DOS environment, the anti-viral methods employed in practice 
are often ad hoc and cannot easily be formalized. VDS makes a judicious 
choice of systematic approaches towards the detection of viruses. It uses 
sophisticated techniques to detect most possible viruses in the DOS 
environment. 
    If you are faced with the problem of recurring virus infections, or have 
data that just cannot be replaced without significant loss, you are invited 
to try VDS on your system. VDS ensures easy detection and eradication with 
little user intervention. With VDS in place, viruses cease to be an 
impediment to productivity.

B. What is VDS?

    VDS is a set of programs designed to contain the spread of computer 
viruses that target PCs running MS/PC DOS 3.0 or above.  VDS works by 
providing early detection and quick recovery. The operation of VDS is not 
virus-specific. In addition, the current implementation does not rely on a 
memory-resident program which degrades the performance of your computer by 
verifying programs every time they are run; however, an independent 
memory-resident scanner is also provided. VDS installs itself on your
system using a special process which checks first for known viruses, and 
then creates a fingerprint of all system areas and executable files. From 
then on, VDS will thoroughly check the system at scheduled intervals and 
will notify you of any suspicious modifications detected regardless of 
whether the virus is a known variant or a new virus altogether.  

C. Why VDS?

-   It is NOT virus-specific.
-   It does NOT need frequent upgrades.
-   It does NOT require much user expertise.
-   It is NOT a TSR (i.e. memory resident) with possible conflicts. This 
    also means that it does not use up precious RAM. The 
    An optional TSR module is provided.
-   It maintains an audit log to pinpoint how a virus entered the system.
-   It can use an external virus signature database for easy updates.
-   It works even when a stealth virus is ACTIVE in memory.
-   It can handle any size DOS disk.
-   It is compatible with DOS 3.0 and above.
-   It supports MS Windows 3.x.
-   It can CAPTURE some memory-resident viruses to speed up diagnosis.
-   It can recover a damaged  partition table easily.
-   It can fix an infected boot sector on the fly.
-   It is blazingly FAST.
-   It includes an automated boot sector recovery tool.
-   It works on Novell Netware, Banyan, and Lantastic network drives.
-   It can usually HEAL itself even when infected.
-   It automatically updates the baseline database after additions/deletions.
-   It can identify most common viruses by name.
-   It can be set to run based on a user-defined schedule.
-   It can remove most known and unknown viruses generically.
-   It can create an emergency diskette for extra safety.
-   It sports a very intuitive object-oriented user interface.
-   It includes a robust integrity checker for ultimate defense against 
    viruses.


D. Components of VDS

    VDS package includes the following components:
          
VDS.EXE 
    An integrity checker that creates a fingerprint database for possible 
    virus targets (programs, boot sectors) and verifies them later for 
    suspicious modifications. In the case of such modifications, the 
    integrity checker offers to restore the affected areas to their original 
    state by using generic disinfection techniques, and backups (for system 
    areas). If the restoration attempt fails, the integrity checker informs 
    the user and requests permission to remove the damaged object by 
    deletion. For example, some overwriting viruses do not preserve the 
    functionality of their victims. To be able to restore such programs, one 
    needs to use the original copies or good backups. In 95% of the cases 
    that involve a virus that can successfully spread, restoration by generic
    disinfection is possible, and guarantees 100% recovery. Viruses that 
    corrupt the operation of their victims get noticed easily and do not 
    tend to get too far.

VDSFSCAN.EXE
    A known and heuristic virus scanner that searches for patterns or code 
    sequences and uses advanced algorithms to identify polymorphic and simple
    viruses inside executable code  such as program files and boot sectors. 
    It can also use a user-defined signature file to permit the addition of 
    newly  discovered viruses.
     
VDSTSR.EXE
    A memory-resident (TSR) program that searches programs before they are 
    run or optionally before they are copied. It also examines the boot 
    sector of a floppy diskette that may have been left in drive A: before 
    warmboot attempts. What's more, it can scan programs being unzipped or 
    de-archived by a compression utility regardless of the version or the 
    maker of such software. In other words, you do not need to update the 
    TSR just because you decided to use a newer release of your favorite 
    file compression utility. It also provides mechanisms to render some 
    stealth viruses inoperable.
   
ISVDSTSR.COM
    A small (17 bytes) program that sets the DOS errorlevel to indicate the 
    presence of the TSR component in memory. The purpose of this program is 
    to allow system administrators in networked environments to enforce 
    loading TSR anti-virus protection on workstations before they are 
    permitted to access programs on a file server.

DUMPSIG.EXE
    A virus signature extraction utility. It is useful when you need to add 
    an external signature.
  
VITALFIX.EXE
    A disk repair utility designed specifically to deal with boot sector 
    infections. It provides the user with various options to eradicate a 
    possible virus, to save and to restore important system information such 
    as the partition table, and to search disks for a possibly relocated copy
    of the boot sector. It is much safer to use this utility than other disk 
    sector editors since it performs sanity checks before overwriting 
    important  sectors on a hard drive.

INSTALL.EXE
    An installation program that automates loading VDS on local and on 
    network drives. It prepares an emergency diskette for your computer so 
    that you can check and restore system areas and program files after 
    booting from a clean floppy diskette. This emergency diskette is
    formatted as a bootable DOS diskette and the required VDS components 
    and fingerprint and recovery information are copied over.

VDSCATCH.BIN     
    A device driver that implements several anti-stealth features and aids 
    VDS integrity checker in maintaining reliable operation even when a 
    stealth virus is active in memory. It also prohibits direct writes to 
    the master and DOS boot sectors as well as low-level format attempts.

                         
                         II. SYSTEM REQUIREMENTS

A. Hardware & Software

    VDS has the following minimum requirements and limitations  to operate
correctly:
   
An IBM PC or compatible computer
MS/PC-DOS 3.0 or higher
384K of available memory
A hard drive (necessary only for integrity checks)
Up to 4000 program files per integrity database (16000 if 192K of extended 
                                                 memory is available)
Up to 32 integrity databases per catalog

    In addition, VDSTSR takes up about 30K of memory when loaded. It can be
loaded into upper memory area under DOS 5.0 or later. VDSCATCH.BIN device 
driver takes up about 300 bytes, and it can also be loaded high.
    Some systems utilize disk compression software to increases the storage 
capacity of drives by compressing and decompressing data on the fly. On such 
systems, you must have the necessary device drivers loaded before VDS. MS-DOS
6.x now includes this optional feature by providing the DoubleSpace interface.
The operation of DoubleSpace is well-integrated into DOS, and works in a 
transparent manner. VDS is tested and found to work as expected on drives 
compressed using DoubleSpace. 

                        
                        III. INSTALLATION

A. INSTALL command line options

    Here is the INSTALL command line options that you can use to set up VDS.
         
INSTALL.EXE     [{-|/}BDEH?MNRUXH]   [src_path]  [dest_path]

-Debug                  Instruct VDS to create a debug trace.
-Banyan                 Install on a Banyan server.
-M                      Use monochrome screen attributes.
-Help or ?              To see the command  line options with examples.
-Emergency <path>       Prepare an emergency diskette.
-Xpress                 Install with default values.
-Uninstall <path>       Remove VDS from the given directory.
-Refresh <path>         Update the VDS emergency diskette for new files
-Network <src> <dest>   Install VDS from the server directory src to the
                        workstation. The .INI files in the src directory
                        will be copied over to the dest directory.

B. Installing VDS on a hard drive

    You will need your bootable DOS diskette (preferably the original), VDS
Distribution diskette, and at least one blank floppy diskette that can go in 
your drive A: for installation. The blank diskette will be formatted and 
prepared as a bootable DOS diskette by VDS. The emergency diskette will be 
used in the case of infections that affect the master boot/partition sector
(if VDS cannot repair it on the fly). 
    The floppy restoration process requires you to use this VDS emergency 
diskette. Some computers have a boot sequence setting in CMOS that allows 
booting from the hard disk even if there is a floppy diskette in drive A:. 
Before starting the installation, please change this setting to boot from 
drive A:. Here are the steps you should follow for proper installation:

1)  Turn the computer off (NOTE: It is very important that you do not perform 
    a warmboot by holding down Ctrl-Alt-Del keys since  a virus can fake a 
    warmboot and stay in memory).

2)  Put the DOS diskette in drive A: (NOTE: The version of DOS on the floppy
    diskette must be the same as the one installed on your hard drive). Turn 
    the computer on. It should boot from the floppy diskette.

3)  If the boot was successful, you should now see the A:> prompt. If the 
    system asks you for time and date, just press Enter  until you are at 
    the A:> prompt.

4)  Remove the DOS diskette and replace it with the VDS distribution diskette.

5)  Type A:INSTALL and press Enter.

*   INSTALL will now complete the installation process by asking you a few 
    questions.

6)  You will see two options: Express setup and custom setup. If you press 
    the Enter key, INSTALL will use the default settings to configure the 
    operation of VDS. Custom setup allows you to modify many parameters to 
    suit your needs.

*   If you have chosen Custom setup, please skip to the next section.

    1. Express Setup:

7)  A configuration file will be created and the necessary files will be 
    transferred to the hard disk in C:\VDSPRO30 directory.

8)  If this is the first time you are installing VDS on your computer, 
    INSTALL will modify  your AUTOEXEC.BAT and CONFIG.SYS to add the lines 
    needed to load, VDSCATCH.BIN, VDSTSR.EXE and run VDS.EXE every time you
    reboot the computer. VDSCATCH.BIN takes up a few hundred bytes.

9)  You will next see the list of files on the hard drive scroll by as VDS 
    scans for infections and creates the baseline profile of all executable 
    files on the disk. There should be lots of disk activity. If VDS finds 
    that there are infected files, you will be asked if VDS should remove 
    them. 

10) INSTALL will ask you if you would like to prepare an emergency diskette. 
    Put a blank diskette in drive A:. MAKE SURE YOU DO NOT HAVE ANYTHING
    YOU NEED ON THIS DISKETTE. It will be formatted as a bootable diskette.
    INSTALL will copy fingerprint databases and the VDS programs to the
    emergency diskette.

11) INSTALL will ask you if you wish to view a tutorial to become familiar 
    with the operation of VDS. If you answer Yes, you will see a few pages 
    of explanation.

12) You can write-protect the emergency diskette at this time and store it 
    in a convenient location. INSTALL will inform you that the computer will 
    restart, please remove any floppy diskettes and then press a key. If VDS 
    is installed correctly, you will see it verify the complete system after 
    the computer boots up. This completes the install process (if you enabled
    floppy booting in CMOS, you can change it back to the hard disk).

    2. Custom Setup:

7)  INSTALL will ask you for the location of VDS distribution files and the 
    home directory for VDS. If the home directory does not exist, INSTALL 
    will ask you if you wish to create it. Type in the desired location where
    VDS should be installed. A configuration file will be created and the 
    necessary files will be transferred to the hard disk in the directory you
    have specified.

8)  If this is the first time you are installing VDS on your computer, 
    INSTALL will ask you if it should modify  your AUTOEXEC.BAT and 
    CONFIG.SYS to add the necessary lines to load VDSCATCH.BIN, VDSTSR.EXE 
    and run VDS.EXE every time you reboot the computer. VDSCATCH.BIN takes 
    up a few hundred bytes. Your original AUTOEXEC.BAT will be saved in 
    AUTOEXEC.VDS, and the original CONFIG.SYS will be saved in CONFIG.VDS.

9)  INSTALL will ask you which drives you wish to protect. You should pick 
    drive C: and any other drives you wish to protect. For each drive you 
    picked, you will see the list of files on the hard drive scroll by as 
    VDS scans for infections and creates the baseline profile of all 
    executable files on the disk. There should be lots of disk activity. 
    If VDS finds that there are infected files, you will be asked if VDS
    should remove them. 

10) INSTALL will ask you if you would like to prepare an emergency diskette. 
    Put a blank diskette in drive A:. MAKE SURE YOU DO NOT HAVE ANYTHING
    YOU NEED ON THIS DISKETTE. It will be formatted as a bootable diskette.
    INSTALL will copy fingerprint databases and the VDS programs to the
    emergency diskette.

11) INSTALL will ask you if you wish to view a tutorial to become familiar 
    with the operation of VDS. If you answer Yes, you will see a few pages 
    of explanation.

12) You can write-protect the emergency diskette at this time and store it 
    in a convenient location. INSTALL will inform you that the computer will 
    restart, please remove any floppy diskettes and then press a key. If VDS 
    is installed correctly, you will see it verify the complete system. This 
    completes the install process (if you enabled floppy booting in CMOS, 
    you can change it back to the hard disk).
  
C. Uninstalling VDS

    You can remove VDS from your hard drive by running the INSTALL program
with the -Uninstall command line option:

    C:\> C:\VDSPRO30\INSTALL   -U   C:\VDSPRO30     <enter>

    If you have performed a custom setup and specified a different directory 
name, then you should substitute that name in the line above. INSTALL checks 
to see if there were other files in the directory before VDS was installed. 
If there were not any, it removes all the files in VDSPRO30 directory, and 
then the directory itself. If there were other files, it displays a warning 
message and aborts without removing any files. It is up to you to delete or 
keep any of those files. You need to perform a "manual" uninstall. Since VDS 
keeps almost all of its files in its own directory, removal is a simple 
procedure. You should also edit your CONFIG.SYS and AUTOEXEC.BAT to remove 
the lines loading VDS components. Your original CONFIG.SYS is renamed to 
CONFIG.VDS, and the original AUTOEXEC.BAT is renamed to AUTOEXEC.VDS during 
installation. You could use them as well; however, if you have installed any 
other programs after VDS, then they might have modified your AUTOEXEC.BAT. 
Be careful before you copy over the CONFIG.VDS and AUTOEXEC.VDS if that is 
the case.  

                      
                      IV. OPERATION of VDS
A. Operational Cycle

    After VDS has been installed on a known-to-be-clean system, a complete
verification of the system areas is done each time the machine is started. 
A daily check of the entire hard disk will also be done, unless you have 
selected a specific frequency in which case a complete check will only be 
performed when the time period has elapsed. For best results, VDS should be 
run from the AUTOEXEC.BAT. It can also be run, just like any other program, 
at the user's discretion.
    The periodic checking requires a computer with a real-time clock that 
can keep track of date even after the computer is turned off. Most systems 
have this capability. On older machines without a real-time clock, the
frequency of checks cannot be specified.  
    The VDSTSR module provides users with the ability to scan programs before
they are run or copied. Once loaded, the user does not need to specify which 
files to scan every time. VDSTSR will intercept requests to execute a program
and will search for known viruses. If it finds an infection, it will post a 
simple warning message and prevent execution or copying of the infected file.
VDSTSR also traps warmboot attempts (CTRL-ALT-DEL) and scans the boot sector 
of the floppy disk in drive A: if one is present. This prevents spread of 
common boot sector infectors such as Stoned and Michelangelo.

B. How does VDS work?

    The first time VDS is installed, a baseline for all executable files and 
the system areas such as the master boot record (MBR), partition table, and 
the boot record (BR) is established. A unique signature is computed for all 
executable objects on the disk. File name, size, date, time and signature are
combined to initialize the records in the database. A similar authentication 
scheme is also used for the VDS program itself. The MBR, partition table, 
boot sector, command interpreter, VDSCATCH.BIN, VDSTSR.EXE and VDS.EXE are 
backed up. The backups will be used if these areas need to be recovered. 
    When VDS is run, it verifies the integrity of its own code. If it finds 
that no tampering has taken place, VDS introduces decoys (small executable 
programs created at run-time) to the system to see if an active virus will 
take the bait. Under normal circumstances, there is no legitimate reason why 
these decoys should be altered by any program. If the decoys are attacked, 
this indicates the presence of a virus with great accuracy. If an active 
virus is detected with this technique, VDS will tell you whether the attacker
was of STEALTH or DUMB variety. If the modifications are masked by the virus,
it is considered to be STEALTH, and DUMB otherwise. VDS uses a proprietary 
verification mechanism to detect if the virus attempted to mask the 
modifications it has made.
    Some viruses do not fall for decoys that easily. In fact, only 
memory-resident program infecting viruses will attack decoys. VDS uses 
different techniques to catch other types of viruses not caught by decoys. 
However, those viruses which do attack the decoys will be captured and placed
in either POV.CCC or POV.XXX (an acronym for Prisoner Of VDS) depending on 
which decoy(s) they attack. POV files can later be used to analyze the 
captured intruder, or for legal purposes. The reason for the strange 
extensions (XXX instead of EXE and CCC instead of COM) is to prevent someone 
from accidentally activating the virus by executing the POV files. If you 
capture an intruder, please mail it to us on a diskette for interrogation, 
i.e. examination! This will allow us to keep track of what viruses are in the
wild, and which areas are affected by certain viruses. You will have
an opportunity to place the captured intruder in a file of your choosing, 
preferably on a floppy diskette so that you can maintain it for further 
evaluation on a test system without any further risk to the computer on which
the virus was found. The captured intruder also makes it simple to extract a 
scan string if it turns out to be a new virus not identified by VDS. You can 
then put the extracted scan string into an external signature database and
search for it on your other disks as well.
    VDS will verify the system areas and all executable files. It will 
generate a report of modified files and newly added files since the last time
VDS was run. The user is given an opportunity to override any alarms that may
be set off. If you have added new files to the machine, then VDS will scan 
each file for known viruses, and if clean, will ask you if you want to add 
the file's signature to the database. If any changes in the form of 
infection, software configuration or addition of files are encountered, VDS 
records them in VDS-STAT.LOG file in the C:\VDSPRO30 directory. This is an 
ASCII text file and can be printed or viewed easily. It contains a date and 
time line showing when VDS was run. It is very useful to check this log when
an infection is discovered to find out how the virus was most likely 
introduced to the system.
    If suspicious modifications appear, VDS attempts to identify any virus(es)
that may be responsible for the changes. A report of all identified viruses 
and the victims affected as well as the date and time of operation will be 
appended to VDS-STAT.LOG file. VDS looks for known viruses in all newly added
files to provide early identification of viruses introduced to the system. 
If no known viruses are identified, then the names of scanned files will be 
written to VDS-STAT.LOG. If a file is determined to be modified, the user 
will be given a chance to restore it. If the restoration attempt fails, then 
you will be able to positively erase it. Positive erase means that the file 
will be overwritten to the end of the last cluster it occupies and then 
deleted. This operation is necessary since DOS leaves the contents of erased 
files intact allowing them to be recovered by a disk utility program. VDS 
prevents infected files from being recovered if you allow VDS to erase them.
    The user can examine reported files at his/her discretion, and take 
whatever action s/he deems necessary. When a possible viral attack is 
detected, our recommendation is to turn off the computer, boot from a clean 
write-protected floppy containing the same version of DOS as your computer 
(preferably the VDS emergency diskette prepared during installation), and 
replace the suspicious files with the originals. In many cases of actual 
virus infection, VDS restoration can easily fix program files completely. 
Note that this generic cleaning approach is very different from 
virus-specific cleaning. It has the capability to recover even from unknown 
virus infections. What's more, VDS double-checks to see if the restoration 
attempt resulted in a full recovery. If not, VDS will warn you about the 
problem. 
    For most boot sector viruses, VDS will restore the partition or boot 
sector automatically using the backup it made during installation. This 
approach effectively takes the guesswork out of MBR/BR recovery. Many other 
programs look for a relocated MBR in a specific sector on the disk and then 
assume that they found the original without being certain. In some cases, 
they cause more damage than the virus could. Not so with VDS. 
    If automatic restoration is not successful, VDS provides a RESTORE option 
that will repair the partition sector using the backup copy saved on VDS 
emergency diskette. If you did not prepare an emergency diskette, and the 
hard disk becomes inaccessible, then you should either use VITALFIX or try a 
manual recovery. In most cases, an experienced computer user can restore the 
disk by following the simple instructions which accompany VDS. As we have 
previously stated, we strongly suggest that you backup your master boot 
record on a floppy diskette so that your recovery will be simple. You can 
use VITALFIX to do this for you if you did not choose to backup your MBR and 
BR during the installation of VDS.


1. VDS command line options

    Here are the command line options that VDS integrity checker accepts:

VDS.EXE   [{-|/}BIRDESVY]   [Drive: | Path]   [{-|/}CX<path>]
   
-Batch Drive:           Check the system areas and the files depending on
                        frequency. This option is the default used during 
                        Express installation. It must be followed by a drive 
                        letter. 
                 
-Install Drive:         Create fingerprint database for the system areas and 
                        the files for a given drive. This option is used by 
                        INSTALL program to start VDS during installation. It 
                        must be followed by a drive letter.

-Rescue                 Use the emergency diskette in drive A: to check the
                        specified drive.
      
-Scan Drive: | Path     Scan for  viruses on the specified drive or path.
      
-Verify Drive: | Path   Perform integrity checks on the specified drive or 
                        path.

-X<path>                Use the specified external signature file, not the 
                        default XTERNAL.SIG.

-C<path>                Use the specified configuration file.

-D  C:  D:              Process multiple drives specified by drive letters.
      
-E                      Use SCSI-compatible code.

-Y                      Create \VDSDEBUG.LOG and report trace of operation.

Examples:
      
To check drive C: for modifications using a non-default configuration file,  
type the following:
      
    VDS  -V  C: -Cc:\integ\vds30.ini
      
To check drive C: using the emergency diskette, type the following:
      
    VDS  -R  C:
         
To scan DOS directory for viruses and use an external signature file, type 
the following:
      
    VDS  -S   -Xc:\virus\mysigs.txt  C:\DOS

To scan C: and D: drives for viruses, type the following:
      
    VDS  -S   -D  C:  D:
         
To perform automatic integrity checks,  include the following line in your
AUTOEXEC.BAT
      
    VDS  -B  C:


2. Configuration (VDSPRO30.INI) file

    Many of the operational parameters for VDS are specified in a file named
VDSPRO30.INI, which can be found in the VDS home directory. This is a simple 
text file and it can be viewed or edited easily using an ASCII text editor. 
Following is an explanation of each line that can be placed in this file.   
    VDS configuration file contains sections marked by certain keywords 
inside square brackets. Currently, the following sections are supported:

    [HOMEDIR]
    [VERIFY]
    [EXT]
    [IGNORE_DIR]
    [IGNORE_FILE]
    [TREE]
    [REPORT]
    [MSG]
    [FLAGS]

    Each section has different requirements for the type of information you 
can enter. The INSTALL program automatically creates an appropriate 
configuration file for you. If you wish to change certain operational 
parameters such as the files that should be excluded from integrity checks, 
you can do so by editing the configuration file with a text editor. Refer to 
the explanation below for details.

; This configuration file specifies operational parameters for VDS Pro.

; VDS.EXE and the system backup files are located in the following directory. 
[HOMEDIR]
C:\VDSPRO30

; Integrity database files are located in the following directory.
[VERIFY]
C:\VDSPRO30

; Files with the following extensions are processed. Adding ??? forces VDS to
scan/check all files.
[EXT]
SCAN = COM,EXE,SYS,OVL,BOO,
VERIFY = COM,EXE,SYS,OVL,BAT,

; Following directories are NOT processed. 
; This is useful in development environments where programs are modified.
[IGNORE_DIR]

; Following files are NOT processed.
; INSTALL defaults to excluding CONFIG.SYS and AUTOEXEC.BAT.
[IGNORE_FILE]
C:\CONFIG.SYS
C:\AUTOEXEC.BAT

; Directory tree(s) are stored in the following directory.
; If you set it to A: or B:, VDS does not store trees.
[TREE]
C:\VDSPRO30

; Messages are written to the following file.
; If you change it to PRN, all messages are sent to the printer.
[REPORT]
C:\VDSPRO30\VDS-STAT.LOG

; Optional message to be displayed if a virus is found
[MSG]
Call System Administrator x5112 ASAP!

; Operational flags
[FLAGS]
; If you wish to maintain integrity information for data files
; set the QUICK_VERIFY to No.
QUICK_VERIFY = Yes
; Look for virus-like code sequences. False positives are likely.
HEURISTIC_CHECK = Yes
; Stop if an infected file is found during scan.
PAUSE = No
; You can eliminate most of the beeps by setting it to No.
BEEP = Yes
; Make sure VDSCATCH.BIN is loaded from your CONFIG.SYS.
ANTI_STEALTH = Yes
; If a modified program file is found, you will need to confirm before recovery.
AUTO_RESTORE = No
; Default is one complete check per day, and system area checks only any
; other time VDS is run with -Batch option.
FREQUENCY = 1
; ENTER key can be assigned to SCAN or VERIFY a file
ENTER_KEY = Scan


C. VDS as a scanner

    VDS integrity checker can serve as an easy-to-use virus scanner that 
works on DOS-compatible drives, including LAN server drives. It offers two 
modes of operation: Interactive and command-line. Interactive mode is based 
on a simple menu system that makes it very easy to access the advanced 
features of VDS, and it offers context-sensitive help (F1 key). Command-line 
mode can also be activated from batch files. VDS accepts various options to 
customize its operation. Once VDS is executed, you can scan multiple 
diskettes easily. 
    VDS presents a very intuitive object-oriented interface based on simple 
menus. By  picking the object you wish to work on, you can exploit the 
powerful features of VDS without any need to consult this manual at all. 
Function keys are assigned to activate certain operations such as scanning 
and verification. Each operation applies to the object currently selected.
    You can move between object selections using the up and down arrow keys.
Pressing ENTER explores a finer level of detail for the members of the parent
object. For example, by highlighting a drive and pressing the ENTER key loads
the subdirectories found on that drive. The ESC key will get you out of a 
menu, or it will ask if you want to stop the search or integrity check 
operation. The CTRL-BREAK key combination will also result in a prompt asking 
if you want to stop the operation.
    We encourage users to start their computer with a clean, write-protected, 
and bootable DOS system diskette prior to using VDS to ensure that no viruses 
are active in memory while scanning. Some viruses manipulate file access and 
try to hide their existence or spread the infection to other programs. 
Although, VDS will attempt to check for such viruses, the only guaranteed way
to do an untampered search is after booting the computer from a clean system
diskette.  
    VDS will also check its own program file to make sure it is not modified.
If it is modified, it will warn you with a message, and it may abort its 
operation. VDS tries to ensure that it is unmodified to ensure correct 
operation.
    In the case of boot sector infections, VDS will ask you if you would like 
to remove an identified virus. This option applies to the master boot sector 
on hard disks and the boot sector on floppy diskettes. You should use the SYS
program included with DOS to remove boot sector infectors from the DOS boot 
record of a hard drive or to keep a system floppy diskette bootable. When VDS
removes a virus from the boot sector of a floppy diskette, it constructs a 
BPB (BIOS Parameter Block) for the diskette and adds instructions to display 
a message you would get from a non-bootable diskette. In any case, the viral 
code will be overwritten. In the case of the hard drive master boot sector, 
VDS keeps the partition table intact and replaces the loader code, again 
overwriting any viral instructions. It will also attempt to verify that the 
partition table actually corresponds to the disk layout.

1. DUMPSIG and external virus signatures

    To facilitate keeping up with new viruses, we have added an external 
signature capability to VDS. This external file is a simple ASCII text file 
and can be viewed or edited easily. You can also use the /Vfilename.ext 
command line option to specify a different path for the external signature 
file. This file can also be used by VDSFSCAN and VFSLITE.  Here is the format
you should use to add a  virus signature entry in this file:

    ; This virus is not stealth
    Disk Muncher
    ; Seems to infect only COM files
    COM
     ; Here is the signature Joe extracted yesterday
    FA 00 23 75 ?? 33 40 B8 ?? 90 90 90 CD 21 

    Lines that start with a ; (semi-colon) are treated as comments and 
ignored. The order of each field is important. In other words, you should 
place the virus name before its type, and the type before the signature. The 
signature is assumed to be in hexadecimal. You can use spaces to separate 
each byte value, or have them in sequence next to each other. The number of 
bytes in the string must be no more than 16, and no less than 8. Wildcard 
characters are accepted. To indicate a wildcard byte, simply put ?? in the 
string. The first byte of the string cannot be a wildcard. 
    The type field can have one of the following values:

    COM
    EXE
    BOTH
    BOOT

    BOTH implies that the virus signature can be found in either COM or EXE 
files. BOOT indicates that the virus attacks Master or DOS boot sectors. 
    VDS tries to read virus information for each entry. To memory 
requirements low, only 32 external signatures can be processed. 
    We will usually provide an updated signature file to our customers. In 
some cases, you may need to add a signature yourself. For example, if a new 
virus infects your computer and VDS captures a sample for you, then you can 
extract a signature and put it in the XTERNAL.SIG. In this way you can 
identify the virus on your disks without upgrading the scanner program. If 
you cannot extract a signature, please send us a sample and we will analyze 
the virus and provide you with a signature and instructions on how to handle 
it. When you extract a signature for a virus, you should take it from the
program entry point on; otherwise, you will need to specify QUICK_SCAN=NO 
option in the configuration file to force VDS to examine each byte of the 
files it scans. If a COM file starts with a JMP instruction, for example, 
you should go to the destination of that jump first. To simplify this 
process, you should use DUMPSIG utility provided in the VDS package.
    Note that some viruses (polymorphic) try to defy signature scanning by 
encrypting and changing themselves. In such cases, it may be necessary to 
update the scanner program. 

DUMPSIG  <filename>

You can redirect the output from DUMPSIG to a text file by using standard DOS
redirection facility as follows:

DUMPSIG  sample.exe   >  sigfile.txt

DUMPSIG outputs 256 bytes from the program entry point of a given file in hex
format. You can then look at the output and pick a 16-byte search pattern; 
you should avoid using a pattern with many repeated values. By testing the 
selected pattern on a few infected samples, you can verify the reliability 
of your string. It is also important that the selected pattern does not 
trigger a false alarm on common files such as those included with DOS; so it 
is a very good idea to test it on DOS program files as well.


D. VDS Device Driver

    VDS creates a device driver for your computer during installation. This 
device driver, named VDSCATCH.BIN, has a very simple purpose: Providing VDS 
with access to the operating system in a manner that is resistant to stealth 
viruses. This is necessary since some viruses have the capability to subvert 
the operating system calls to hide the modifications they have made to the 
programs. When such a beast is active in memory, it will look as though none 
of the programs are infected. By recording operating system access points 
very early in the startup process, VDSCATCH.BIN enhances the reliability
of VDS scanner and integrity checker.  The memory requirement for this 
device driver is quite frugal, about 300 bytes!
    Another function of this device driver is to disallow tracing certain key
interrupts. Many stealth viruses use the trace mode available on the Intel 
80x86 CPUs. This way, they can bypass monitoring software and spread 
undetected. VDSCATCH.BIN attempts to stop such tricks. Note that some 
anti-virus packages use tracing as well, and they may complain.

E. VDSTSR

    VDSTSR provides memory-resident virus scanning before execution or 
copying of files as well as floppy diskette boot sectors before a warmboot 
attempt. If it determines that the file that is about to be run or copied 
contains a known virus, it will warn the user showing the name of the virus 
and then deny the request.
    The purpose of VDSTSR is to prevent introduction of viruses to PCs in a
transparent manner. In other words, the user need not run a virus scanner 
manually every time he/she runs a program or copies new files to his/her 
hard/floppy disk. If there is a floppy diskette containing a boot sector 
virus in drive A: and the user attempts to warmboot the computer without 
opening the drive door first, VDSTSR scans the floppy diskette for boot 
sector viruses and issues a warning. This effectively prevents infections
from common boot sector viruses such as Stoned and Michelangelo.
    As a side effect of this type of mechanism, copy operations will be 
slowed down by about 50% depending on the system configuration. The apparent 
time delay in program loading, however, should be negligible. Optionally, 
the user can specify not to scan upon copy operations but only before 
execution of programs. This approach is recommended since it provides most of
the protection without overall performance degradation of the computer system.
The default behavior is not to scan during copy operations.
    Another side effect is the memory required to keep all virus signatures 
and names in RAM. Although the code is barely 4K, the signature database 
takes up about 30K. The good news is that, VDSTSR can be loaded high under 
DOS 5.0 and above, therefore not using up any of the precious 640K 
conventional memory. 
    To keep the program size to a minimum, VDSTSR only provides a simple
message displaying the virus name and the program as well as producing a beep
on the system speaker to get the user's attention. It does not provide any 
options to unload it from memory or support other fancy but rarely used 
features. VDSTSR does not scan for complicated polymorphic viruses, either. 
Following example illustrates a typical case:

C:\TEST\FRODO.EXE
<beep> 4096 virus found in FRODO.EXE
Access denied <pause>

    The last message comes from COMMAND.COM since VDSTSR issued an error
code as response to the request to execute the program file FRODO.EXE.
    During copy operations, the following message would be displayed:

COPY C:\TEST\FRODO.EXE  FRODO2.EXE
<beep> 4096 virus found in FRODO.EXE
Invalid function <pause>

    If the user hits the Ctrl-Alt-Del key combination in order to reboot, and 
there is a floppy diskette in drive A: with an infected boot sector, a message
such as the following is displayed:

<beep> Stoned-2 virus found in floppy diskette boot sector.
Remove the floppy diskette from drive A: now! <pause>

    VDSTSR has only one command line option and does not require any special
procedure to install. It requires DOS 3.0 or higher to operate. 

    VDSTSR   [/COPY]

    The default is not to scan during copy operations, but only before 
program execution and warmboot attempts. VDSTSR should be placed in the 
AUTOEXEC.BAT file before any other TSRs except network drivers and disk 
compression drivers.
    A small utility program called ISVDSTSR.COM is supplied to allow system
administrators in LAN environments to check if VDSTSR is loaded on a 
workstation before granting permission to login. All this tiny program does 
is issue a request to VDSTSR and see if it is answered properly, indicating 
that VDSTSR is operational in memory. If everything is working fine, ISVDSTSR
will set DOS error level to 1. This can be used in a batch file as follows:

ISVDSTSR.COM
if errorlevel == 1 goto LOADED
echo You have not loaded VDSTSR on your system. You cannot login.
logout
:LOADED


F. VDSFSCAN

    VDSFSCAN is an easy-to-use virus scanner that works on DOS-compatible 
drives, including LAN server drives. It comes in two flavors: Interactive 
and command-line. Interactive version is implemented by the VDSFSCAN.EXE, 
and the command-line version is provided by VFSLITE.EXE.
    Both programs share a common configuration file named VDSFSCAN.INI. This
is an ASCII text file that modifies the operation of  the scanner. You can 
edit the settings in the INI file to tailor it to your needs. VFSLITE is very
useful in networked environments where a post-login scan is desired. It sets 
DOS error level so that the result of scanning can be checked in a batch file.

1. Command line options

    VDSFSCAN accepts the following command line options:

VDSFSCAN.EXE  [{-|/}Lcd]  [{-|/}LRV<filename>] 
              [{-|/}ABCDEGH?NPQUZ]  [{-|/}Fnn] [drive: | Path]  

-A       All files regardless of type
-B       Break/ESC is NOT allowed
-C       Complete file scan
-D       Scan all local drives starting with C:  
-E       Erase infected files   
-Fnn     Frequency of scanning in days (0-30). Default is 0, scan every time.
-G       Perform heuristic scan. Off by default.
-H or ?  Help for command line options
-L       Path of error log file. Default is C:\VDS-ELOG.TXT
-N       No memory scan. On by default.
-P       Do NOT pause. Default is pause.   
-Q       Quiet scan. Do not beep.
-R       Output report. If no file is given, C:\VFS-STAT.LOG is used.
-S       Recursively scan subdirectories. Off by default.
-U       Upper memory scan (as well as base memory)
-V       Virus signature file. VFSLITE always looks for XTERNAL.SIG first.
-Z       OEM DOS compatibility mode

    If run without any command line parameters, VDSFSCAN offers a menu-driven
interface.


G. VFSLITE

    VFSLITE is the command-line-only edition of VDSFSCAN. It does not have 
the elaborate menus with different colors, context-sensitive help, and other 
features that the regular VDSFSCAN has.  VFSLITE is light only in its user 
interface, not its capabilities. In fact, it detects the same number of 
viruses as VDSFSCAN. It is slightly faster in operation, and it makes an 
ideal anti-virus tool for networked environments where a post-login scan is 
desired. It sets the DOS errorlevel to 1 if it finds a virus, just like
VDSFSCAN. You can test this in a batch file and take appropriate actions 
such as denying access to the file server.

1. Options and default settings

    The command line options are almost the same for VDSFSCAN. An INI file 
can be used to establish a consistent set of flag settings for everyone. 
When VDSFSCAN or VFSLITE starts, they look for an INI file named VDSFSCAN.INI
in the same directory as the program. If it is not present, they look for the
same file in the current directory. If it is not found in the current 
directory either, they use internal default settings. Since the INI file is 
processed first, the command line options can still override the settings in 
the INI file.

    The default internal flag settings for VFSLITE are as follows:

LCD screen = No
Pause = Yes
Allow Break = Yes
Memory scan = Yes
Upper memory scan = No
Beep = Yes
Frequency of scan = 0 (every time)
Quarantine infected files = No
Generate report file = No
Whole file scan = No
Multiple floppy scan = No
All files scan = No
Erase infected files automatically = No
Heuristic scan = No

    Note that the frequency of scan is also new. Before, only the integrity 
checker component of VDS allowed this. The frequency option works by creating
and updating a file called C:\VDSFREQ.TXT. This text file has one line showing
the last date and time of virus scan. It is updated as necessary. For this 
option to work correctly, the computer must have a hard drive and a 
battery-backed real-time clock. Most systems are equipped with such devices. 
If the frequency is set to 0, VFSLITE ignores the frequency file; otherwise, 
it will create or update it accordingly.

2. Configuration (VDSFSCAN.INI) file

    The VDSFSCAN.INI file is a simple text file with the following format and
entries:

1.  Lines that start with a ; (semi-colon) are comments, and they are ignored.
2.  Each keyword should be flushed to left and followed by an = (equal) sign.
3.  After the equal sign, an appropriate value should follow. The value 
    depends on the type of the entry, such as log file name, or a YES/NO.
4.  Upper or lower case can be used interchangeably. Spaces are ignored.
5.  Value only entries for directories and files to be ignored.   

    Another convenient feature is that you can include your own message in 
the .INI file. This message will be displayed if a virus is discovered. For 
example, the number to the help desk could be displayed.

    Here is a sample .INI file:
   
; This is an INI file for VDSFSCAN-Lite 3.0
; It contains entries for flag settings that guide the program operation

; On laptops, set the following to Yes for easier-to-read screen output.
LCDSCREEN = No

; Message to display when a virus is found. Leave blank after = if none.
ALERTMSG=Call system administrator x5112 ASAP! You have a virus.

; Report should be sent to the following file. Leave blank after = if none.
REPORT=C:\VFS-STAT.LOG

; File for the user-defined signatures. Leave blank after = if none.
EXTSIGS=C:\XTERNAL.SIG

; Quarantine directory where the infected/suspicious files are copied
QUARANTINE=C:\VDS-CELL

; Ignore the following directories
IGNOREDIR=1
C:\CODE

; Ignore the following files
IGNOREFILE=2
C:\CONFIG.SYS
C:\AUTOEXEC.BAT

; Frequency of scanning in days. Must be between 1-30. 0 means scan every time.
FREQUENCY=0

; Files are scanned entirely or partially. Leave it at partial (No) normally.
FULLSCAN=No

; Which files to scan. Normally, set it to No.
ALLSCAN=No

; Scan all local drives starting with C: if no command line parameters are given.
LOCALSCAN=No

; Scan base memory.
MEMSCAN=Yes

; Scan upper memory.
UMBSCAN=No

; Pause if a virus is discovered or an error has occurred.
PAUSE=Yes

; Allow user to stop scanning.
ALLOWBREAK=Yes

; Beep if a virus is discovered or an error has occurred.
BEEP=Yes

; Remove infected files. If PAUSE is set to No above, it is automatic.
ERASEFILE=No

; Heuristic scan is on by default. Set it to No if causes false positives.
HEURISTICSCAN=Yes

3. Command line options

    VFSLITE accepts the following command line options:

VFSLITE.EXE  [{-|/}R|V<filename>] [{-|/}ABCDEGH?LMNPQUZ] [{-|/}Fnn] 
             [drive: | Path]  

-A       All files regardless of type
-B       Break/ESC is NOT allowed
-C       Complete file scan
-D       Drives to scan follows. If no drives given, scan all local drives 
         starting with C:  
-E       Erase infected files   
-Fnn     Frequency of scanning in days (0-30). Default is 0, scan every time.
-G       Perform heuristic scan. Off by default.
-H or ?  Help for command line options
-L       LCD screen attributes should be used not color
-M       Multiple floppy diskettes will be scanned. Ask for the next disk.
-N       No memory scan
-P       Do NOT pause. Default is pause.   
-Q       Quiet scan. Do not beep.
-R       Output report. If no file is given, C:\VFS-STAT.LOG is used.
-U       Upper memory scan (as well as base memory)
-V       Virus signature file. VFSLITE always looks for XTERNAL.SIG first.
-Z       Zoo-test. Log both infected and clean files during scan.

Examples:

To scan drive D:
    VFSLITE  D:
 
To scan drive C once every three days:
    VFSLITE  -F3  C:

To scan drives C: and D:
    VFSLITE  -D  C: D:

To scan all local drives starting with C:
    VFSLITE  -D

To scan all files on drive C:
    VFSLITE  -A  C:

To scan C:\DOS directory:
    VFSLITE  C:\DOS
 
To scan multiple diskettes in drive A::
    VFSLITE  -M  A:

To scan entire contents of files on C:
    VFSLITE  -C  C:
 
To erase infected files on C:
    VFSLITE  -E  C:
 
To disable beep sound and scan drive C:
    VFSLITE  -Q  C:

To scan drive C: without pause (useful during "zoo" testing):
    VFSLITE  -P  C: 

To specify a non-default external signature file:
    VFSLITE  -Vf:\vds30\mysigs.sig  C:

To specify a non-default report file:
    VFSLITE  -Rc:\results.vds  C:

To scan drive C: and put the results in VFS-STAT.LOG file:
    VFSLITE  -R  C:

To skip memory scan and scan drive C:
    VFSLITE  -N  C:

To scan base and upper memory and drive C:
    VFSLITE  -U  C:

To see this help message:
    VFSLITE  -H

4. DOS errorlevels returned

    To facilitate use of VFSLITE in batch files, DOS errorlevel is set as 
follows:

errorlevel = 0     No viruses found
errorlevel = 1     Infected/suspicious files found
errorlevel = 2     Self-check failed

Here is an example batch file:
   
VFSLITE  C:
if errorlevel = 2 goto PROBLEM
if errorlevel = 1 goto VIRUS  

goto END

:VIRUS
echo You might have a computer virus. Call help desk at 5112 ASAP!
pause
goto END

:PROBLEM
echo Virus scanner is damaged. Call help desk at 5112 to get a new copy!
pause

:END

5. Differences between VDSFSCAN and VFSLITE options

    There are a few command line options that work differently in VDSFSCAN.
Some of these options are available only in one or the other; while others 
have a completely different purpose. 

-M  Instructs VFSLITE to scan multiple floppy disks, asking for the next disk 
    after each one. VDSFSCAN does not have this option.
-S  Instructs VDSFSCAN to recursively scan subdirectories within directories.
    VFSLITE does not recognize this option, although it functions as if -S is
    specified.
-L  Instructs VFSLITE to use monochrome attributes. VDSFSCAN accepts this
    option as "Log errors".  VDSFSCAN uses -LCD instead.
-D  VFSLITE allows drives to be specified following this option. VDSFSCAN
    interprets it as "Scan all local drives". Note that VFSLITE will also 
    scan all local drives if no drives are specified.
-Z  Instructs VDSFSCAN to use compatibility mode for decoy launching. VFSLITE
    interprets it as "Zoo-test" option, which forces every scanned file  to 
    be reported in the log. This option is for testing purposes only.
    

H. How to use VITALFIX

    VITALFIX is a utility program designed to automate recovery from an MBR
(master boot record) infection, and to allow the user to perform low level 
operations on a hard disk such as sector editing. It can place a fresh copy 
of MBR code without disturbing the existing partition table. It can backup an
MBR to a file on a floppy diskette. It even allows you to take a clean MBR 
from one computer, and a partition table from an infected one, combine them
together and put it back on the infected system, effectively replacing the 
viral code while leaving the partition table intact. This is possible since 
most computers partitioned using the same FDISK program will contain similar 
code, and differ only in the contents of their partition tables. 
    If you simply let VITALFIX construct an MBR for you, you will have our 
MBR code placed on your disk. Since this piece of code has to do "standard" 
stuff, there should not be any problems. Please let us know if it does not 
work on your system. We have tested it on several IBM computers and 
compatibles with a variety of hard disks.
    VITALFIX is a menu-driven program. You simply highlight the option you 
are interested in and press enter. You could also press the first letter of 
an option to activate it. Context-sensitive help is available by pressing the
F1 key.
    VITALFIX has some interesting features such as the capability to search 
for a relocated MBR all over a hard disk and to view the contents of any 
given sector. You can also write contents of a file to a sector and vice 
versa. It also allows you to edit sectors. Please be very careful when doing 
any write operations since a simple mistake could damage your data.
    You should always boot the computer from a write-protected, clean system
diskette before using VITALFIX. This will eliminate any memory resident 
viruses or programs that may interfere with disk operations. 

1. Command line options

VITALFIX has the following command line options:

VITALFIX [{-|/}X | LCD | H | ?]

-X       Compatibility mode. Use INT 13h.
-LCD     Use monochrome attributes.
-H or ?  Display command line options.


I. Scenarios and Messages

    During its operation, VDS may issue several warning messages. Following 
is a list of scenarios that will highlight common warnings, their reasons, 
and recommended actions to take.

Message: Partition sector modified. Will attempt to restore.
Reason:  There is a good chance that either a partition sector infector has 
         entered the system, or some other damage to the partition sector 
         has occurred. 
Action:  VDS will attempt to restore the partition sector and reboot the 
         system. If the verification fails again, VDS will abort the 
         restoration attempt and recommend a floppy recovery using the VDS 
         emergency diskette.

Message: No message, VDS simply hangs the machine.
Reason:  If VDS has been running just fine, but stopped functioning now, then
         VDS.EXE may be corrupted either by accident or by an overwriting 
         virus which failed to preserve its victim's operation. It is also 
         possible that some TSR program caused a conflict. Assuming VDS runs 
         as the first program in your AUTOEXEC.BAT file, and CONFIG.SYS is 
         not modified, you should assume the worst case: a virus attack.
Action:  Reboot the computer from VDS emergency diskette or a write-protected 
         known-to-be-clean system diskette. If you have prepared the VDS 
         emergency diskette, then run VDS from A drive with the CURE option:

               A:\VDS  -C  <enter>

              * You can simply run REPAIR.BAT

Message: VDS requires DOS 3.0 or higher to run.
Reason:  The version of DOS installed on your computer was below 3.0.
Action:  You need to upgrade to DOS 3.0 or above. VDS will not run on systems 
         with a lower DOS version.

Message: Error occurred during installation.
Reason:  This is a generic message that indicates a malfunction during 
         installation.
Action:  You should see some other error messages come up before this one. 
         The cause can be determined based on those. Go back and check if 
         you followed all the steps in the installation procedure.

Message: Different DOS version. If you upgraded DOS, reinstall VDS.
Reason:  DOS version during installation was different from the current one.
Action:  The system floppy used during installation should have the same DOS 
         version you have on the hard disk.

Message: Need 1 megabyte free space on hard disk to install VDS.
Reason:  VDS found that there is not enough space on the hard disk.
Action:  You should delete some files to free up space and then run INSTALL 
         again.


J. Common Questions and Answers

    This section addresses some common questions about VDS.

Q - Do I have to know a lot about viruses to be able to use VDS on my
    system?

A - Not at all. One of the design goals was to create a program that can be 
    easily used by novice computer users. Viruses present some unique 
    complexities even to the experienced computer security experts. VDS can 
    alleviate most virus-related problems automatically. You are, however, 
    encouraged to become familiar with general guidelines to deal with 
    computer viruses.

Q - Can I run VDS under MS Windows 3.x?

A - Yes, you can. We recommend that you either create a PIF file with full 
    window option on, or shell to DOS first. Do not try to switch tasks while
    VDS.EXE is running. VDSFSCAN can run in the background in 386 enhanced 
    mode. VITALFIX should never be run from inside Windows since it accesses 
    the hard disk directly.

Q - Is VDS compatible with DOS 6.x?

A - Yes, indeed!  We have tested VDS on various systems running MS/PC DOS 3.0.
    3.1, 3.2, 3.3, 4.01, 5.0, and 6.0. We did not encounter any problems. 
    Please let us know if you do.

Q - Can I run VDS under OS/2?

A - Maybe on systems with FAT file systems, not HPFS. You can run it in OS/2
    DOS box in a limited fashion. Extensive testing under OS/2 is not done.

Q - I have a program that requires to be run before other programs in
    AUTOEXEC.BAT. Since VDS should be the first program to run, how
    can I resolve this conflict?

A - There is no conflict from a technical point of view. The other programs 
    that force you to run them first usually re-vector several interrupts to 
    their memory resident code. If another program grabs these interrupts, 
    then they would not be able to guarantee proper operation. Running VDS 
    as the first program does not affect these programs since VDS is not 
    memory-resident and it does not hook any interrupts. If you run other 
    resident programs, however, they may conflict with the operation of VDS. 
    The solution is to run VDS as the very first program in AUTOEXEC.BAT. 
    Remember that the other programs need protection against viruses as well.
    If VDS runs first, it can check them before a possibly infected program 
    is run. If VDS itself is infected, it will notice that fact and warn you.

Q - Does VITALFIX work on IDE drives?

A - Yes, it does. VITALFIX is compatible with all types of hard drives 
    currently in use. This includes drives with MFM, RLL, IDE, SCSI, and 
    ESDI controllers. The only problem we have come across was on disks that 
    used a compression or security program that rendered the disk unreadable 
    unless all access was done through the interface these programs provided.
    VITALFIX cannot tolerate such restrictions since it must have direct 
    access to the bare drive. Anything less would open up a security loophole
    if a virus is active when VITALFIX is operating. It is always a good idea
    to boot the computer from the original DOS diskette before using VITALFIX.
    As a precaution, VITALFIX checks the partition table to find out if the 
    drive has any non-DOS partitions, and will warn you if this is the case.
    In some cases, the partition table may not be available to make that
    determination. If you know you have non-DOS partitions or compressed
    partitions, we strongly suggest that you do not use VITALFIX to perform 
    any of the functions that involve writes to the disk.

Q - My computer is infected with a virus already. How can I use VDS to
    deal with this problem?

A - The approach to this problem depends on what kind of a virus you are 
    dealing with. VDS can help you locate which parts of the system are 
    affected if it is a virus that can be identified using our search strings. 
    If it is a boot sector infector, you can simply turn off the computer, 
    boot from a write-protected floppy diskette and run SYS program to put a 
    clean boot sector onto your hard drive. If it is a program file infector,
    you need to replace the infected files from the original distribution 
    diskettes. In the case of partition sector viruses, we recommend that you
    use VITALFIX.EXE. This utility automates locating MBR, and even 
    constructs one if necessary. 
    You may be able to get the original partition sector back, if the virus 
    relocated it to another sector on track 0, head 0 (as some do). You need 
    to fire up a low-level disk editor, and look through head 0, track 0. 
    The first sector contains the Master Boot Record (partition sector), and 
    may have been replaced by the virus code. Look at each sector (17 of them
    on an MFM drive), and see if any one has AA55 as the last two bytes in 
    the sector. These identification bytes are present on all legitimate 
    partition sectors as well as boot sectors. Remember that this is a 
    trial-and-error process, so it may not work. You may want to seek 
    assistance from a local computer "guru" if necessary. Make sure you save 
    the current copy of the partition sector on a floppy diskette first. 
    If the hard disk is accessible after booting from a floppy diskette, 
    then the partition table (64 bytes near the end of the master boot 
    record) may still be valid.
    The code that loads the active boot sector may belong to the virus. If 
    you can extract the partition table information from the current copy of 
    the partition sector, you may even be able to place it into a good 
    partition sector you get from a similar computer with a similar disk. 
    You can then place this combination of partition table from the infected 
    system and partition sector code from the clean system on top of the 
    current partition sector on the infected system and reboot. This might 
    just do the trick. Be very careful, however, and backup all your data
    files before starting this surgical operation. You might end up clearing 
    the MBR and repartitioning the disk as a last resort. 


Q - Does VDS have a TURBO mode versus a SECURE mode?

A - Yes. If you set QUICK_VERIFY=YES in the configuration file, VDS will
    operate in TURBO verification mode, which is faster but less accurate 
    than VERIFY mode. Turbo mode is not recommended for data integrity.

Q - How secure is VDS encryption scheme?

A - Our purpose was not to come up with an unbreakable (if there is any such
    scheme) encryption method, but to use something more secure than good old
    XOR. Contrary to popular belief, the robustness of an anti-viral 
    integrity system cannot be measured by the sophistication of the 
    encryption algorithm it uses. Some people even believe that they can deal
    with stealth viruses easily if they use an encryption scheme that cannot
    be forged. That is not so. The stealth viruses intercept the verification
    routine's attempts to access the modified executables on the disk, and 
    present them with a clean copy. No matter how sophisticated the algorithm
    used to generate a signature is, it will be fooled every time since the 
    verifier is getting clean (the same as the original) input. While these
    people are perfecting the technique to compute a one-way cipher of 
    extreme complexity, stealth viruses are having a ball on the disk they 
    choose to invade. Of course, if a direct attack is a concern, then more 
    secure encryption methods are very useful. In the DOS environment, 
    manipulating the disk access is much easier and works in most cases. So, 
    if someone tells you they got a superior multi-stage encryption routine 
    that can come up with secure keys for their anti-viral product, just ask 
    them why they chose to waste their time on such an endeavor!  Viruses
    are not an attack to the secrecy but to the integrity and availability of
    computer systems. Unfortunately, many self-proclaimed experts seem to 
    confuse these separate issues.

Q - I heard some programs create hidden files on the disk. Does VDS
    create any hidden files?

A - Absolutely not. We have nothing to hide from the end-users!  Almost 
    everything VDS creates is restricted to the VDS home directory. Decoys 
    and report files may be created in the root directory as well.

Q - Does the VDS authentication scheme eliminate the possibility of a
    trojan version of the program?

A - To some extent. "Trojanization" has been a problem with many software
    packages in the market. VDS authentication scheme provides a reasonable
    amount of assurance that the copy you have is actually created by the 
    original developers. It is possible to circumvent this mechanism and 
    display a fake message. This can be considered a direct attack. Remember,
    a direct attack against any program is possible (you can safely ignore 
    those who claim otherwise). The purpose is to provide another layer of 
    security. If every software product in the market put in as much effort 
    as VDS does, there would be less incidents of trojans. You should get 
    your programs from reliable sources. If you see a program claiming to do 
    major database work, and it is only 4K long, you should double-check on it!

Q - I backup my hard disk regularly. Do I still need an anti-viral program
    to be safe?

A - Yes, you still need a program such as VDS. Backups can help when 
    recovering from damage. The problem is by the time you notice that the 
    system is infected, the virus may have been transferred to the backup 
    media. When you restore the system, you may very well restore the virus 
    too!  In some cases, the virus may corrupt the backup diskettes and 
    render them useless. One person reported that Stoned virus corrupted all 
    his backup diskettes while he tried to backup his hard disk to be able to
    perform a low-level format. Unfortunately, the Stoned virus was active in
    memory at the time. By the way, when was the last time you verified that 
    you can actually restore from your backups?

Q - What are "POV" files?

A - POV stands for "Prisoner Of VDS". These files are created by VDS when it
    detects an active virus in memory that attacks upon file access. When VDS
    introduces decoys into the system, some viruses immediately attack them. 
    VDS notices this fact and captures the intruder in a file. VDS will also 
    capture a modified boot or partition sector in POVBOOT.BBB or POVPART.PPP
    file in the VDS home directory. This feature speeds up the diagnosis 
    process. In other words, you will have the captured virus stored in a 
    file that you can analyze (or have someone analyze it since this would 
    require familiarity with the 80x86 assembly language). Remember that not 
    every virus can be caught this way. If you catch a virus, you are 
    encouraged to mail it on a diskette to us for analysis.

Q - My company wants to purchase VDS for all our PCs, but we are not
    sure if there is an expiration date on use of VDS?  Is it necessary to
    renew the VDS site license on a regular basis?

A - We believe that the end-user has a right to run the version of a program 
    he paid for as long as he is satisfied with its operation. For updated 
    copies of VDS, we offer different licensing agreements.

Q - Is it possible for a data file to become infected by a virus?

A - The criteria for a virus to do anything at all is that it must gain 
    control of the CPU. An ordinary data file will never have such control. 
    The possibility exists for macro or script files that some application 
    software packages provide to automate certain operations. There are no 
    common viruses that exploit this feature. Another possibility is to cause
    damage as a side effect, for example, by redefining a key sequence as a 
    substitute for a destructive command, assuming a driver such as ANSI.SYS 
    is loaded. Again, these are very limited ways that a virus can propagate,
    if at all. Batch files can also be used to activate a program that
    contains a virus. The problem is that it is too obvious and will be 
    detected easily.

    
K. Known Problems and Conflicts

    This section addresses various conflicts or problems with the operation 
of VDS that we are aware of. You are encouraged to report any problems you 
discover.

1. SETVER.EXE that comes with MS/PC DOS 5.0 causes false alarms.

    SETVER.EXE program modifies itself to keep track of programs and the 
version of DOS they should get as a result of INT 21h, function 30h call. 
Many consider such self-modifying programs "ill-behaved". Until developers 
of DOS come up with a better way to accomplish the same task, you are likely 
to get false alarms. We do not intend to accommodate use of such a 
questionable practice.

2. When scanning a Netware volume, VDS reports an ERROR condition on some files.

    Certain files such as NET$OBJ.SYS are open and locked by the Netware
operating system. They contain bindery information. Any attempt to open them 
will result in an error condition. You should not be concerned since this is 
a feature not a bug!

3. Some programs are reported to be suspicious when I enable the HEURISTIC_SCAN.

    Heuristic scan is a method that allows early recognition of viral code. 
Certain coding techniques are common to many viruses. By looking for such 
indications, VDS is able to recognize some new viruses. The problem is that 
there may be legitimate programs that also use such code. The only guaranteed
way to establish whether a virus is present is by performing an analysis of 
the suspected program.  We try to minimize such false alarms, and we would be
interested in hearing from you if you come across a suspicious file.

                     
                     V. VIRUS ATTACK METHODS

A. Virus defined

    A virus is a piece of  programming code that has the ability to replicate 
itself by attaching to other executable objects, either by logical or physical
means. In addition to its replication task, a virus may have a manipulation 
task in the form of a damage routine. Most PC viruses are written in the 
80x86 assembly language to keep their size small and to gain greater 
flexibility in manipulating the operating system and other program files.
    Researchers classify PC viruses in several ways. We prefer to separate 
the structure of the implementation of viruses from the objects they attack. 
We classify them simply by their features and types.

B. Features of PC Viruses

    There are several features of  PC viruses:
            
1. Stealth Virus:

    A virus that has the capability to hide the modifications it has made to 
its victims to evade detection. For example, the virus may hide the file size
increase when the user attempts to get a  directory listing. Another example 
would be a boot sector virus that returns the original boot sector when a 
program attempts to read it. To accomplish such tricks, a stealth virus 
usually stays resident in memory and monitors disk access either at the DOS 
or BIOS level. This way, it can see each disk access request and alter the 
results to hide the modifications it has made. There are varying degrees of 
stealth capability. In other words, it may be possible to discover the 
presence of a virus using an alternate mechanism to examine the object that 
may have been affected.
   
2. Dumb Virus:

    A virus with no stealth capability. Such a virus makes no attempts to 
conceal its presence. The most apparent change is the increase in file size 
since the virus added its code to the program file. An alert user can notice 
such a change easily. This is the most common feature of  PC viruses.
   
3. Encryptive Virus:

    A virus that keeps its code encrypted and includes a decryptor to restore 
itself. The purpose of encryption is to make it difficult to extract a scan 
string. The decryption routine is designed to contain variable sections so 
that it is not easily  recognized. It is possible to detect such viruses 
using a wildcard pattern that matches the decryptor.
   
4. Polymorphic Virus:

    A virus that keeps its code encrypted and includes a highly variable 
decryptor to restore itself. It is not possible to extract a wildcard scan 
string to recognize the decryptor. One has to design an appropriate algorithm
to detect it. We usually analyze the structure of the decryptor and identify 
its key features, and then use this information to implement a detection 
routine.

C. Types of PC Viruses

    There are three major types of PC viruses:
   
1. MBR/BR Virus:

    A virus that attacks the master boot record or the DOS boot record of a 
disk. This type of virus usually moves the original contents of the boot 
sector and replaces it with its own code. Key data structures within the 
boot sector (partition table or BIOS parameter block) are almost always left 
intact not to mess up the operation of DOS. A boot sector virus reserves 
memory for itself by reducing the base memory size (e.g., 640K to 638K), and 
copies its code to the top of memory. There are a few boot sector viruses
that remain in low memory as well. Almost all boot sector viruses monitor the
BIOS disk interrupt (INT 13h) to spread or to hide themselves. Every time a 
disk is accessed, they get control and check if the disk being accessed is 
already infected. If not, they can infect it before returning control to the 
original interrupt handler.
   
2. Program Infector:

    A virus that attaches to program files. There are a few subcategories for 
this type of viruses:            

a. Simple Infector: 

    A virus that modifies a program file physically to add its code. The 
program file entry point is adjusted so that the virus gets control when the 
program is executed.
      
b. Companion Virus: 

    A virus that logically inserts itself into the search path so that it 
gets control when the user attempts to run a program that has the same file 
name. The most common variety exploits the fact that DOS runs a program file 
with a COM extension rather than the one with an EXE extension if both of 
them exist. Another possibility is to insert the virus in the search path. 
If the user does not specify the exact location of the program, then DOS will
use the path to look for it. If the virus program comes before the actual
program in the search path, then the virus will get executed. This type of 
virus is rare indeed.
      
c. System Infector: 

    A virus that alters DOS system data structures so that it gets control 
instead of the program the user intends to run. For example, DIR-2 virus 
manipulates the directory entries to point the starting cluster to its 
location. When DOS reads the disk to load a program, the virus gets loaded. 
Another possibility is to insert  the virus in a system location that DOS is 
known to always load.

3. Multi-partite Virus:

    A virus that can infect both program files and boot sector of a disk. 
Dealing with such a virus can be quite a nuisance since the first portion of 
the virus gets control of the system even before DOS is loaded. The virus can
alter the system vectors to implement a potent stealth mechanism, for example.
Removing this type of virus requires that all affected areas are restored.

D. Some facts about viruses

1. PC-based local area networks are NOT immune to viral attacks.

    Network connections pose another question by making it easier for the 
virus to travel from one location to another. As long as the user has write 
access to the programs on a disk, it may be able to infect it. If the program
file happens to be on a file server, all those that run it may cause the 
virus to jump to their local machines. Can you imagine what could happen if 
the superuser/supervisor runs an infected program on the LAN by mistake?
    It is a misconception that PC-based networks are less susceptible to 
viruses. The boundaries of information flow are not always well-defined. 
Although many popular LAN operating systems provide various control 
mechanisms that can be used to implement robust anti-viral measures, many 
sites do not take advantage of them. If the users allow each other to access 
one another's directories, for example, the risk of infection is very
high, and the rate of infection may be even higher compared to spread via 
floppy diskettes. Since many common viruses employ "ill-behaved" programming 
techniques, they cannot infect network file servers even when write/modify 
access is granted. This does not eliminate the risk by any means, but simply 
makes it less evident.

2. Electronic bulletin boards do not necessarily contain infected software.

    There have been some extreme remarks about the dangers of down-loading
software from electronic bulletin boards (BBS). In actuality, the sysop (the 
person that maintains the BBS) has to take pains to ensure his board is free 
of malicious software to be able to keep a good reputation. On the other hand,
there are supposedly some hacker BBSs that provide viruses, even in source 
code. Your chance of bumping into one of these is very little. Please do not 
be afraid to explore what the BBSs in your area have to offer. Many useful 
programs such as VDS are available for the cost of a local phone call. There
is no need to be paranoid about the situation, just be aware of the 
possibilities. It is always a good idea to get software only from 
well-recognized bulletin boards such as the ones maintained by user groups. 
It is a good practice to search the programs you down-load for known viruses.

3. Write-protected floppy diskettes cannot be infected by a virus as long as
the floppy drive is working correctly.

    This is why you should always place a write-protect tab on all original 
diskettes if they are not already protected. The spread of viruses can be 
effectively slowed down by careful use of appropriate control mechanisms.

              
              VI. PARTITION/BOOT SECTOR INFECTIONS

A. Preliminary information

    It seems that there is much confusion about the difference between a 
partition sector (Master Boot Record is another name for it) and a boot 
sector among many PC users. If you are already familiar with the organization
of a typical hard disk, you can skip the rest of this section; otherwise, 
please read on.
    The very first sector on a typical hard disk stores the partition 
information for the disk. Within the partition sector, a 64-byte area 
contains enough information to locate all physical partitions on the disk, 
and shows which partition is the active partition. The active partition is 
used to boot the computer. There can be four physical partitions on
a disk. The partition sector is located outside of any partition boundaries 
and has enough code to determine the active partition, load the boot sector 
in that partition and transfer control to it. The code in the partition 
sector does not care which operating system it is loading. In fact, one 
reason for having partitions is to allow coexistence of multiple operating 
systems on one hard disk. FDISK program that comes with DOS is used to
manipulate the partition table.
    Each partition has a boot sector. The boot sector holds certain 
information about that partition (in an area called BIOS Parameter Block or 
BPB) such as the number of sectors and number of FATs (file allocation table).
In the case of the active partition, it also contains some code that loads 
the operating system. DOS partitions can be either primary or extended 
(extended partitions were added in DOS 3.3). The extended partition can be 
further subdivided into logical drives.
    FORMAT program with the /S option is used to make the active DOS 
partition bootable by setting up the necessary operating system files. 
FORMAT must also be run on every partition to be able store files. This is 
called high-level formatting. Floppy disks do not have partition sectors, 
they only have a boot sector. That's one reason low-level and high-level 
formatting is combined into one procedure in the case of floppy diskettes.
    Since the partition sector contains vital information to access the drive, 
it is important that this information be protected. If you lose your partition 
sector, you might have to wipe out the MBR, and repartition the disk. Of 
course, this operation would make all files inaccessible. Fortunately, it is 
hardly ever necessary to take such an extreme step. If you have VDS in place,
you should be able to restore your partition table information easily.
    Nevertheless, if you cannot reconstruct the partition table so that you 
can backup your files, or if you just want to get rid of a virus residing in 
the MBR, you should know a few important facts. 
    1.   A complete low level format of the entire hard disk is not necessary.
Using a low level disk editor, you can write zeroes over the contents of the 
MBR and repartition the disk. This will get rid of the virus. In fact, 
certain types of hard drives, namely IDE, are not designed to be low level 
formatted by the end-user. Low level format is necessary on brand new drives 
that do not come pre-formatted from the manufacturer. Getting rid of an MBR 
virus is just a matter of removing its code from MBR and putting a fresh copy
of the standard MBR code.
    2.   FDISK will not put a fresh copy of the MBR code if the disk is 
already partitioned; therefore, an MBR virus can survive repartitioning by 
standard FDISK. This might surprise you, but it is a fact so dangerous to 
ignore. Worse yet, FDISK will destroy the boot records and FATs of any 
modified partitions. For example, if you repartition a drive with exactly 
the same parameters, you will still lose access to your files. 
    
    ***  MS/PC DOS 5.0 and higher includes an improved version of the FDISK
         program. It can replace the MBR code only, while leaving the 
         partition table intact. Unfortunately, the DOS technical 
         documentation does not mention this capability. The command is:

                   FDISK   /MBR

    3.   If the partition table is intact, as is the case in most infections, 
you can recover all your data easily. To do this, you should use a utility 
like VITALFIX, or do it manually following the instructions in this document.
For details, see the section titled MANUAL RECOVERY PROCEDURE under HOW TO 
DEAL WITH VIRUSES.

    
    Following diagram illustrates the organization of a typical hard disk.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  Master Boot Record               ³ Sec 1, Cyl 0, Head 0
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³                                   ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ 
     ³  Active Partition Boot Sector     ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³  File Allocation Table 1 (FAT#1)  ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ Partition 1
     ³  File Allocation Table 2 (FAT#2)  ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³  Root Directory                   ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³                                   ³
     ³       Data Area for files         ³
     ³                                   ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³  Other Partition Boot Sector      ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³  FAT#1                            ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ 
     ³  FAT#2                            ³ Partition 2
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³  Root Directory                   ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³                                   ³
     ³    Data Area for files            ³
     ³                                   ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     
     B. How to recover with RESTORE option

    If the partition table or the boot sector is modified, you can restore it
    as follows:

    1.   Turn off the computer.
    2.   Place the write-protected VDS emergency diskette in drive A.
    3.   Turn on the computer.
    4.   Run  VDS. 

              A:\VDS  -R  <enter>

    VDS will attempt to use the backup copy of the affected area to restore 
it. If it detects that the backup copy is also modified, it will abort the 
restoration attempt so as not to do more harm than good! The restoration 
process involves the partition sector, boot sector on the active partition, 
and COMMAND.COM. 

    5.   If all goes well, VDS will ask you to remove any floppy diskettes 
         and press a key to reboot the system. All system areas should pass 
         the verification tests this time. If they do not, the restoration 
         attempt was unsuccessful, and a manual recovery is necessary.

C. Manual Recovery Procedure

    This section assumes you have a standard system partitioned using FDISK, 
    and running MS/PC DOS 3.0 or above. If you have a hard drive with a 
    non-standard geometry, then the following procedure may be more 
    complicated. Exercise caution during this recovery procedure, since you 
    could accidentally render your disk unusable. If you can access the hard 
    disk after booting the computer from a floppy diskette, you should backup
    all your data files first.

    If you know or suspect that your hard drive is infected by a virus, you 
can attempt to restore it by carefully verifying that each point in the 
execution path during start-up is clean. To do that, you need to know what 
points are in the execution path. Refer to the diagram below.
    First get a write-protected (preferably the original) DOS system diskette.
You cannot format a diskette on a possibly infected system, and be positive 
that the diskette does not get infected. Some viruses stay in memory and 
infect the floppy diskettes whenever they are accessed. Turn the computer OFF.
Place the system diskette in drive A: and close the drive door. Turn the 
computer ON. Never trust that a warm-boot (Ctrl-Alt-Del) will get rid of a 
memory resident virus. Some viruses are known to fake a warm-boot. Worse yet,
some vicious viruses activate their damage routine when you press 
Ctrl-Alt-Del combination. 
    The purpose of the following procedure is to clean the system areas of a 
computer with a hard disk so that it is safe to boot from the hard disk. 
Verification of other program files are not considered in this discussion. 
Recommended recovery procedure for infected program files is to replace them 
with the originals. A utility program such as VDSFSCAN that searches for 
infected programs can speed up the process. Virus cleaning utilities are
NOT recommended. If you know or suspect that a program is infected, copy over
the original from the distribution diskette. This is the cleanest and the 
safest approach. If you have installed VDS integrity checker on your system, 
it could restore most programs to their original state easily and reliably; 
even new viruses can be removed with this procedure.
    To attempt recovery, you will need a low level disk editor that allows 
you to read and write any sector on the disk. If you feel intimidated by 
manipulating your disk in this manner, please do not attempt a manual 
recovery without the help of a friend who has experience performing this 
type of an operation. Nevertheless, VITALFIX is very handy to do such low 
level manipulations. 

    
    On a standard PC, the startup sequence looks like the following:

    Stage 1.

          point A             point B                   
    
       ÉÍÍÍÍÍÍÍÍÍÍÍÍ»      ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿               
       º  ROM       º      ³  Master    ³               
       º            º      ³  Boot      ³               
       º  BIOS      º      ³  Record    ³               
       º            º      ³  Code      ³               
       º  CODE      º      ³  [0, 0, 1] ³               
       º            º      ³            ³               
       º            º      ³            ³               
       ÈÍÍÍÍÍÍÍÍÍÍÍÍ¼      ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ               
  
    Stage 2.

          point C         point D        point E
       ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿    
       ³ Boot       ³  ³ IBMBIO.COM³  ³ IBMDOS.COM ³    
       ³ Record     ³  ³    or     ³  ³    or      ³    
       ³ Code in    ³  ³ IO.SYS    ³  ³ MSDOS.SYS  ³    
       ³ Active     ³  ³           ³  ³            ³    
       ³ Partition  ³  ³           ³  ³            ³    
       ³            ³  ³           ³  ³            ³    
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ    
       
          point F         point G          point H      
      
       ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
       ³ Device     ³  ³ COMMAND.COM ³  ³ Programs      ³       
       ³ Drivers    ³  ³             ³  ³ in            ³      
       ³ in         ³  ³             ³  ³ AUTOEXEC.BAT  ³       
       ³ CONFIG.SYS ³  ³             ³  ³               ³
       ³            ³  ³             ³  ³               ³
       ³            ³  ³             ³  ³               ³
       ³            ³  ³             ³  ³               ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


    Stage 1 is independent of any operating system. Point A is implemented in
hardware and is not modifiable, therefore it cannot be infected. At point B, 
the code resides on the hard disk (head 0, cylinder 0, sector 1). The purpose
of point B is to provide a mechanism to load different operating systems. You
can have your disk partitioned so that one partition is for DOS, while another
one is for some other operating system. By marking one of them as active in 
the partition table (located within the Master Boot Record), you can control 
which operating system will load upon bootup. The code in MBR simply locates 
the active partition by examining the partition table, loads the code in the 
boot sector of that partition and transfers control to it. The MBR is 
attacked by viruses such as Stoned since it provides very early control of 
the system. More sophisticated viruses can easily redirect BIOS disk access 
routines (the vector addresses reside in the first 1024 bytes of RAM and are 
modifiable) to evade detection. 
    Stage 2 is where a specific operating system comes into play. In the case
of DOS, the code at point C loads the first system file (IBMBIO.COM) and 
transfers control to it. After initializing the DOS kernel, IBMBIO.COM 
processes the CONFIG.SYS file. Each device driver listed in CONFIG.SYS is 
loaded and initialized. IBMDOS.COM is also loaded at this time. At point G, 
COMMAND.COM gets control and processes AUTOEXEC.BAT file if there is one.
Except for point A, all other points in the execution path are modifiable. 
You must assume that any modifiable code is prone to viral infections. During
recovery you must assume the worst case and handle each point as if it is 
infected by a virus. You must also remember that a higher point depends on a 
lower point. In other words, if you do not clean point B, you cannot 
guarantee that point C will not be compromised afterwards. 
   The MBR code (point B) is easily replaceable. The key item at point B is 
the partition table which contains vital information to access the disk. If 
the hard disk is accessible after booting from a floppy (e.g., DIR C: works
fine), then there is a good chance the partition table is intact. You should 
immediately extract the partition table information (64 bytes total) from the
first sector on head 0, cylinder 0 and store it in a file on a floppy 
diskette. If you have a similar (uninfected) computer with a hard disk, you
should make a copy of its MBR in a file. The next step is to combine the 
partition table that you stored away with the clean MBR you have taken from 
the uninfected computer. The result is an uninfected MBR that can be used to 
replace the infected one. Make sure when you combine the two pieces, you are 
editing at the correct offset within the MBR sector. Our VITALFIX utility 
automates this whole process (except swapping diskettes, of course!). Here is
a simple picture to clear things up:

                       Master Boot Record

         Sector 1 on head 0, cylinder 0

                               partition table
         1                447                512
          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÑÍÍÍÑÍÍÑÍÍÍÑÍÍÍÍÍÍ»
          º                 ³   ³   ³  ³   ³ AA   º
          º   MBR Code      ³ 1 ³ 2 ³ 3³ 4 ³ 55   º
          º                 ³   ³   ³  ³   ³      º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÏÍÍÍÏÍÍÏÍÍÍÏÍÍÍÍÍÍ¼

    Note that the partition table has four entries making it possible to 
divide the disk into four distinct areas. The MBR code is the same on most 
PCs as long as you use the same FDISK program. The partition table depends 
on how the disk is set up. The last two bytes must be AA55 by convention.
    Some viruses simply relocate the whole MBR sector to another location on 
the disk, then place their code in sector 1, head 0, cylinder 0. They also 
redirect disk access routines and present the original copy when someone 
attempts to access the MBR. This is an evasion technique used by certain 
viruses that target the MBR. Since you have booted from a clean floppy 
diskette, you do not have to worry about this. If you can find the original 
MBR on the disk (usually relocated to another sector on head 0, cylinder 0),
then you could simply put it back to sector 1, head 0, cylinder 0 to recover. 
For example, one variant of Stoned virus places the original MBR to sector 7, 
head 0, cylinder 0. In that case, follow the procedure outlined above.
    Once you restore the MBR, you can move on to point C and verify it. The 
easiest way to accomplish that is to use SYS.COM program included with DOS. 
SYS will put a fresh copy of the boot sector code as well as replacing IO.SYS
and MSDOS.SYS. This operation cleans points C, D, and E (three birds with one
stone).
    Point F involves verifying each device driver listed in the CONFIG.SYS 
file. Unless you need a device driver to access the disk due to non-standard 
geometry, you can simply delete (or rename) CONFIG.SYS. Otherwise, you have 
to copy the device drivers from the original diskettes to the hard disk. Make
sure you are copying over the ones that CONFIG.SYS activates.
    Point G is easy to take care of by copying COMMAND.COM from the original
DOS diskette to the hard disk. If you have a shell statement in CONFIG.SYS 
that specifies a different command interpreter, then make sure you replace 
that one with the original.
    Point H can be handled by deleting (or renaming) AUTOEXEC.BAT since it is
not required.
    Now the system is ready to be booted from the hard disk without 
reactivating a possible virus. Of course, the first time you run an infected 
program, everything you have cleaned so far might get reinfected. Did we say 
dealing with viruses can be a little tricky?

                  
                  VII. HOW TO DEAL WITH VIRUSES

A. Recommended Guidelines

    When dealing with viruses, there are a few rules to go by, all of which 
make good common sense. These rules are:

1.  If there is a possibility that your hard drive is infected, do not use a
    floppy diskette on that computer unless it is write-protected.

    Rationale:     If you did NOT cold-boot the computer from a clean floppy
                   diskette, the virus may be active in memory and it can 
                   infect the floppy diskettes used in the drives. This is, 
                   after all, a common way for spreading infections among 
                   computers.

2.  Do not boot a hard drive system from a floppy diskette unless you are
    positive that the floppy is virus-free.

    Rationale:     This follows from Rule #1. The virus can infect the hard 
                   disk. The result is a hard disk that passes on the virus 
                   to other floppies. The floppy can carry a boot sector 
                   virus even if it was not formatted to be a system diskette,
                   because all DOS diskettes have a boot sector.

3.  If your PC is connected to a local area network, and you detect that
    your system may be infected by a virus, disconnect your PC from the
    network immediately.

    Rationale:     The purpose is to isolate the infection in order to 
                   minimize the spread, and reduce the time required to clean
                   the system. Make sure you know how to disconnect only your
                   PC. Pulling out the wrong cable may bring down a whole 
                   subsection of the network.

4.  If you receive new programs (especially games), test them on a machine 
    that does not have valuable data before installing these programs on 
    other computers.

    Rationale:     This precaution will help prevent the introduction of new 
                   viruses into the system. Even shrink-wrapped software may 
                   contain a virus. There have been some unfortunate 
                   incidents where major computer companies shipped infected 
                   diskettes to their customers by mistake.

5.  If you do not feel technically competent to handle a virus attack,
    contact someone who can help.

    Rationale:     Dealing with viruses can be a very tricky business. You 
                   cannot afford to leave a single infected file on your 
                   system. It takes only one infected program to continue 
                   the spread of the virus.

6.  When you want to backup your hard disk, boot from a write-protected, 
    clean floppy diskette. Preferably use file-by-file backup mode instead 
    of image backup.

    Rationale:     Some viruses remain active in memory and interfere with 
                   disk access. They are likely to corrupt the backup 
                   diskettes. File-by-file mode gives you a better chance to 
                   recover damaged backups.

7.  Write protect all original diskettes as well as their backups before
    using them.

    Rationale:     This would prevent infection of your program diskettes 
                   should they be used in an infected system. Besides, during
                   recovery you can be assured that the originals are not 
                   corrupted.

8.  Before using programs that came on floppy diskettes, search them for
    known viruses.

    Rationale:     Many companies are just beginning to realize the threat 
                   the viruses pose. They may or may not have a virus-free 
                   program development environment. It is better not to take 
                   any chances and check the diskettes yourself. If you find 
                   a write-protected, original program diskette to be 
                   infected, first contact the company that sold you the disk
                   and complain.

9.  If your BIOS supports choosing a default disk to boot, set it to C:.

    Rationale:     This will eliminate the possibility of inadvertently 
                   booting from an infected floppy diskette left in drive A:.
                   Some modern BIOSes offer a setup option that allows you to
                   always boot from your hard disk, even if there is a floppy
                   diskette in drive A:. Many common boot sector infectors 
                   like the Stoned virus can infect your hard disk only if 
                   you boot your computer from an infected floppy diskette.