CyberSpace Transporter

                     (C) Copyright 1993-1995 Frances Decatur
                              All rights reserved 
                                   Version 6.4

                                  April 28, 1995

          
          This documentation and associated programs are the property of 
       Frances Decatur. 
          
       
       What's NEW
       ====================================================================
       Ver 6.4
       Added option for registered users who DO NOT want their REAL
       NAME displayed in "Registered To:" When entering your Name in
       CYBER.CFG preceed it with *BBS*
       Example:
       *BBS*Joe User  - Will display BBS Name instead
       or
       Joe User  - Will display Joe User

       Ver 6.x
       Fixed problem with the door being closed and still dropping DTR
       on the outgoing modem. 
       Added notice to user when door is closed or modem in use.
          
       CST will no longer hang up on a SLIP connection!

       The ~ script command will send just a CR and not a CR/LF after
       sending a string. This is useful for systems that cannot handle
       the CR/LF pair (IE: Unix systems)

       A User may type "EXITCST" if he\she gets stuck on a system.
       This will hang up the dial-out modem and return the user to the 
       CST menu. You may want to inform the user of this command in an
       intro or custom menu screen.

       CST will now SCAN for an unused COM port and use it!!
       
       MAJOR CHANGES TO THE CONFIG FILES!!!  (see cyber.cfg & port.#)

       See Multiline BBS's for info on LAN and OS/2 based systems


       Problems & Technical Support??
       ====================================================================
       Reading the docs because your having problems?

       In order to serve you better and faster I will need the following:
       
       CONFIG.SYS, AUTOEXEC.BAT, CYBER.CFG, CYBER.BAT (or the batch file 
       you use to load the Transporter), a DOOR.SYS or DORINFOx.DEF (which
       ever you use) generated by your BBS, an explnation of the problem 
       to include:
                  Exactly what does it do or not do!
                  What is on your screen!
                  What message does CST display!
                  What modems do you use?
                  What Com ports?
                  Address and IRQ for each port!
                  Any other info you may find important.

       When you have this all together, Zip-ARJ-Whatever it into 1 file
       and crash mail to 1:268/348 or attach them to email (upload) on 
                        
                        The Circuit Board 717-676-9339  
       
                  Most problems can be handled in this manner. 
       
       Voice support is available to registered and non-registered users
       only through the BBS #. Logon and page the sysop. I will usually
       be available 8am - 10:30am and 7pm - 9pm. 

       I'LL DO MY BEST TO GET YOU RUNNING! At the time of this writing 99% 
       of all problems reported have been resolved. The 1% didn't bother to
       follow up, may be up and running, or may have fallen through the 
       cracks?
       
       If your getting an ERROR "62" check your *.cfg files. One of them
       is too short, and therefore wrong. In some cases the DOOR.SYS has
       been found to be too short.

       If your using the X00 fossil driver, you map ports as follows:

               X00 E 0=add,irq 1=add,irq 2=add,irq etc,etc

                       where..
                              0=COM 1 \
                              1=COM 2  \
                              2=COM 3   > if they exist
                              etc      /
                              etc     /
                             add=Hex address of the port (ie:3F8,2E8,etc)
                             irq=Dec IRQ of the port  (ie:3,4,5,7,whatever)

              
       
       

       What is CyberSpace Transporter?
       ====================================================================
          CyberSpace Transporter is a door that allows your users to call
          out to other systems on a second modem and phone line. Most of
          your callers may be long distance to BBS's that are local to you.
          So now you can actually save your users some REAL MONEY. And 
          maybe make some for yourself.
                                      
       What is Shareware?
       ====================================================================
          The shareware concept is great for both programmer and the end-
          user. The programmers can distribute their product without
          getting involved in expensive marketing or advertising. The end-
          user benefits by receiving a full-featured program, usually
          better than the commercial competition, and support available
          directly from the author. But it only works if the end-user
          participates in the shareware concept.

          Shareware is not free. After using the CyberSpace Transporter
          for a 30 day trial period, you must pay for continued use of 
          the program. I have worked hard to produce a good program, 
          and the price is very fair. Especially considering that many of
          your users could save more than the price of registration...
          EVERY MONTH!! 
          
          CyberSpace Transporter will only allow 10 minute calls until
          it's registered! Along with some annoying delays!

       Support            
       ====================================================================
          If your having problems setting up and running CyberSpace 
          Transporter, support is available! 
          (see the beginning of this document)

      #*  The Circuit Board   Feedback           717-676-9339   
       *  Internet            cst@cktbd.de.com
          Compuserve          72510,2363
       #* FIDOnet             Sysop@1:268/348

       *  Mail read daily.
       #  Latest version will always be available here. Freq CST.ZIP

          Voice support is available ONLY when there is no other way.


       Disclaimer            
       ====================================================================

          CyberSpace Transporter and all support files (REGISTERED OR
          UNREGISTERED) are provided on an "AS-IS" basis with no 
          warranty. Frances Decatur cannot accept responsiblity for loss 
          of data, profit, or any damages which are incurred by the use 
          of this program or any support files.

       Modem Info   
       ====================================================================

          CyberSpace Transporter requires that all highspeed modems be
          set for RTS/CTS handshaking.

          Your modem should be set to reflect the TRUE state of carrier
          (not forced true) and dropping DTR must hang up the modem!
         
         !!-------------------------------------------------------------!!      
               NOTE: If CST reports the "MODEM is in use", and it
                     is not. Then this is not been set! Sending AT&C1
                     to the modem and saving it will solve this problem.
                     This command is the only command CST cannot send to 
                     modem itself, as if a carrier is persent it WILL 
                     NOT use that port. Using the command AT&F ANYWHERE
                     even in other programs will reset this. If you MUST
                     use AT&F in any program that uses the modem then 
                     use AT&F&C1&D2.
                      
                     If CST does not hang up the modem, then AT&D2 should
                     be sent to  the modem. This could be done in the dial
                     string. IE: AT&D2DT or AT&D2DP
         !!-------------------------------------------------------------!!      
          
          If you setup your system with a highspeed modem and a 2400 modem,
          your DOOR.SYS must have line 2 as "actual connect rate" and line 5
          as locked port speed. If your BBS does not write DOOR.SYS in this
          way, 300 & 1200 baud callers (if any) may have data loss 
          problems.

          DOOR.SYS is the only drop file that will report both the callers
          connect rate and the actual port speed. This is why DOOR.SYS
          is used.

          CST will also support DORINFOx.DEF dropfiles. Because dorinfo.def
          files do not support both callers connect rate and modem to 
          computer rate, results may be unpredictible. Problems may arise
          if you use a high speed modem and a 2400 baud modem. If your
          modems both support rts/cts handshaking CST should function just
          fine.

       MultiLine BBS's   
       ====================================================================
       
       CST can be setup to share modems with other BBS nodes. 
       
       CST will first check to see if a carrier is present (if the node 
       is in use). If it is, the user of the Transporter will be informed 
       the modem is in use and the program will terminate. If not, the 
       Transporter will execute the command specified in the CYBER.CFG 
       file to close a window. When it is through it will execute the 
       command specified to open the window.

       If you have more than 3 Nodes, then closing and opening windows
       can get messy. If 2 users are in the transporter at the same time
       then the window numbering can become confused. I recommend you
       create a batch file to open and another to close a window. In
       the close batch file for a node you should close the window in 
       question and open a small window to hold it's place. In the batch 
       file to re-open the window you should close the place hold window 
       and reopen the Node window. Use these batch files in the PORT.x
       file. This applies to the recommended DV Utilities and may or may 
       not be needed with other utilities.
       
       This has been tested under Desqview. In other operating systems
       you would need to find utilities to shutdown and re-start the BBS
       program that is also using the modem CST will dial out on.

         !!-------------------------------------------------------------!!      
           NOTE:
                If a user dials out and the modem resets and hangs up,
                VERIFY the BBS Node that is also using the modem has been
                shutdown. In most cases if CST dials out and a BBS node
                is still running on that modem, the BBS software will
                reset and hang up the modem!
         !!-------------------------------------------------------------!!      

       OS/2 Utilities:
     
       If you know of any utilities to open and close an OS/2 window
       from another window, PLEASE let CST support KNOW! As of this 
       writing there are none. Since OS/2 protects the port your only
       choice is to install 2 modems for EVERY OS/2 window using CST.

       LAN Utilities:

       Stomper 2.31 will allow sharing of modems on a LAN. CST will
       scan these ports for an open modem and use it. The commercial
       modem server version is not needed for dial out. CST will do 
       the hunting for a dial out port. This could be used to setup 
       a modem server for dialout using the private version. 
       
       Desqview utilities:
       
       I have tested the Transporter using the following...

       DVSI's KILL.COM to close the window.
       
       KILL <# of the window>
       
       
       DVUTIL to open the window

       DVUTIL -o <pif keys>

       Both of these utilities are avalable on The Circuit Board as
       well as many other BBS's

       DVSI and DVUTIL are NOT part of CyberSpace Transporter! They
       are seprate utilities by different authors. Other utilities
       may be available these are just the ones I have used to test 
       this feature.

       If your running a mailer or for some reason want to prevent
       CST from closing a window see 1.7 Closing the transporter.

       Closing the Transporter            
       ====================================================================

       Creating a file called NOT.NOW in the cyber directory will close 
       the Transporter. A user can enter the door and go to the menu. 
       But when he chooses a system to call, will be informed the 
       transporter is closed.

       It does not matter what is in the file as long as it exists.
       A simple way to create one would be:

       dir >>c:\cyber\not.now

       This can be used to close the transporter for any reason, such as a 
       mailer tossing, etc. If your sharing your voice phone line you may
       want to set this up as an event during peak voice call hours. CST
       does NOT answer the phone if it rings.
       
       Setting up            
       ====================================================================

          The first thing you need to do is create a directory where 
          CyberSpace Transporter will live. [ie: c:\bbs\cyber]
          Copy CYBER.EXE and CYBER.DOC to the directory you just created.

          Create a batch file to load CST.
          Example:

          c:
          cd\bbs\cyber
          cyber C:\BBS\DOOR.SYS
          c:
          cd\bbs
         
         !!-------------------------------------------------------------!!      
           NOTE:
                If you don't usually load a FOSSIL then you can load and
                unload it here.
         !!-------------------------------------------------------------!!      

       
       2.1 Configuration CYBER.CFG  
       ====================================================================

       A new CYBER.CFG! ONLY 1 for all nodes!

       CYBER.CFG:

       Line 1: BBS Name
       Line 2: Sysop Name
                          
                          For registered users who DO NOT want their REAL
                          NAME displayed in "Registered To:" When entering 
                          your Name here preceed it with *BBS*
                          Example:
                          *BBS*Joe User  - Will display BBS Name instead
                          Joe User  - Will display Joe User
       
       Line 3: Trial security level (see Trial Accounts)
       Line 4: Hangup while in Xport (Y/N)
    ** Line 5: security level to dial ANY #

WARNING ->**    This entry will allow a user to enter any phone number
                at all!! Including long distance and international numbers.
                To restrict this by security level create a text file named
                seclevel.any
                In this file list the 1st 3 numbers a user with that sec 
                level can dial. One per line.

                example for security level of 20:

                20.any:

                676
                839
                894

                In this example any user with a security level of 20 will
                be able to enter any phone number beginning with 676, 839, 
                or 894. If the first 3 numbers of the number he wants to 
                dial are not any of these 3, CST will return to the main 
                menu.

   
       NEW PORT.# file - 1 for every port CST can use!

       create PORT.1, PORT.2, PORT.3, ETC for all available dial out ports
       
       Port.x:

              com port #              <-COM port to dial out on 
              Connect string          <-STRING sent by modem upon connect
              Maxbaud                 <-max speed of outgoing modem
              dial string             <-dial string (ATDT)
            * kill a window (Y/N)     <-use opn/cls hooks 
            * Kill command            <-close window command
            * Open Command            <-open window command
              Additional string       <-additional string sent b4 dial str 
              additional string delay <-seconds to delay after above is sent

        * NOTE: see Multiline BBS
       
       Example:   
             
             2                   <-COM port to dial out on 
             CONNECT             <-CONNECT STRING string (dial out modem)
             19200               <-max speed of outgoing modem
             ATM1DT              <-dial string
             N                   <-use opn/cls hooks for Desqview(Y/N)
             kill 3              <-close window command
             dvutil -o v2        <-open window command
             AT&D2               <-additional string sent b4 dial str
             5                   <-seconds to delay after above is sent
                
                NOTE:
                The additional string will be sent to the modem before
                the dial command and system number. This can be used
                to send init strings, or anything common to all systems.

                The delay must be long enough for the modem to finish
                executing the string before the regular dial string is sent.

                Say you send "AT&D2DT18005551212,,,,9;" to the modem using
                the additional string. The delay MUST be long enough for
                the modem to dial and process all the delays (,) before the
                regular string is sent. Otherwise the modem will never 
                process the regular dial command.
          



          SYSTEM.CFG holds the names, numbers, and security level of
          each system you make available to your users. A max of 255
          systems can be specified.

          SYSTEM.CFG:

                Brinkman's Hollow  <- 1st system name
                6893123            <- phone #
                20                 <- access type
                Pocono             <- 2nd system name
                8394055            <- phone #
                20                 <- access type
                etc
                etc
                etc

       Accesss Types
       -------------

       number     Access by Security Level
       ------

       Place a number here and CST will compare it to the users 
       secutity level
       
       
       @          Access by Password
       -
       
       "@password" the user will be prompted to enter an access code.
        this code is whatever follows the @
       
       example:
       Cool BBS
       555-1212
       @Cyber

       In this case when a user attempts to call the Cool BBS, he will be
       prompted to enter an access code. If the used does not enter
       "Cyber" (case sensitive) then he will be informed he does not
       have access to that system.

       
       
       *          Access by list of names
       -
       
       Cyberspace Transporter will look in the cyber directory for
       a file named <System # as appears in menu> If this file has the 
       users name (case sensitive to name in door.sys) it will allow him 
       to dial that system. 

       example:
       system.cfg -
                    un cool bbs
                    555-2121
                    20
                    real cool bbs
                    555-1212
                    *
       2.dat -
                    Joe User
                    Jim Decatur
                    John Doe
       
       In this case Joe User, Jim Decatur, and John Doe are the only
       users that will be able to access real cool BBS.


       
       %          Access via Script File
       -
       usage: %name

       "name" being the name of the files with out extention. CST will
       look in the cyber directory for "name".scr and "name".dat

       .dat  this file should list the names of users who have access
             to this system. One per line. It is case sensitive (to the 
             user name in DOOR.SYS)
             The word ALL on any line will open the system to all.

       .scr  this is the script file. CST will dial the number and upon 
             connection look to this file for instruction. Nothing will
             be passed from the BBS to the user (except # commands) until 
             this script has finished. This is a text file and one command 
             per line.

       
       Script file commands:

       !  Expect text
                        !password: 
                        CST will wait until it recieves "password:"

       *  Expect text and send a CR every 2 seconds
                        *password: 
                        CST will wait until it recieves "password:"
                        It will send a CR every 2 seconds until it sees
                        the string your expecting.
                        This is useful for ADP's Autonet Login and
                        some Unix system login's.
       
       ^  Expect text and wait 15 seconds then skip

                        ^menu? 
                        
                        CST will wait 15 seconds for "menu?". If it
                        sees "menu?" it will send a CR. If not it will
                        skip and return to the next script command.
       
       @  send 
                        @abcd
                        CST will send "abcd" plus a carriage return/line 
                        feed to the transporter modem only.
       
       ~  sendnolf 
                        ~abcd
                        CST will send "abcd" plus a carriage return to
                        the transporter modem only.
       
       #  send user
                        #Please Wait
                        CST will send "Please Wait" plus a carriage return
                        to the USER only.

       $  send ascii #
                        $10
                        CST will send the ascii character = to the ascii code
                        10 to the bbs.
                        see an ascii code chart.

       % delay
                        %10
                        will delay 10 seconds 
       
       
       The following examples have been included in CSTd.ZIP:

       CIS.SCR for connecting to Compuserve via CIS network
       DELPHI.SCR for connecting to Delphi via SprintNet

       Edit the username and passwords for your application.


       &        Access Script file then dial #
       - 

       This is almost the same as a regular script file. Difference being
       this will execute the script file first, then when it has completed,
       dial the number in systems.cfg.
       
       This is useful for accessing Bell Alantic Ultra Call Forwarding
       services, and the reason it has been included. It may also be
       useful for sending specific information about a BBS before the
       number is dialed via a script file.
       
         !!-------------------------------------------------------------!!      
           NOTE:
                The file WERKS.SCR (included) shows an example of
                using Bell Alantic Ultra Call Forwarding to access
                a BBS system.
         !!-------------------------------------------------------------!!      
       
       A file called RESET.ME will be droped in the cyber directory when
       this option is used. I have my cyber.bat check for this file and 
       open a new DV window to run a utility to reset the Call Forwarding
       number back to my bbs. This is a very small file, and if you find
       you have no use for it you can have your cyber.bat delete it or just
       leave it there.

       Access assistance for networking
       --------------------------------

       If the mailer a sysop uses for FIDO, QWK, or other types of
       networks is capable of using log-on scripts, it is possible that CST
       will be able to assist in lowering their costs!
       
       After the copyright screen CST will look for the file "NETWORK.DAT", 
       if it exists in the cyber directory CST will check to see if the 
       users name is in the file. If so, it will send the INTRO.ANS/ASC 
       screen and bypass the menu screen and dial the system found in 
       NETWORK.DAT. 
       
       After the call is completed it will display the EXIT.ANS/ASC and exit 
       the door.
       
         !!-------------------------------------------------------------!!      
           NOTE:
                This is also useful if you use CST to access only 1
                system, such as an Internet provider. You could also 
                setup CST in 2 different directories, 1 for normal use
                and 1 to provide access to a specific system.
         !!-------------------------------------------------------------!!      
       
       format:
                            User Name (case sensitive to name in door.sys)
                            System # from menu to dial
                            Username
                            system #
                            etc
                            etc

         !!-------------------------------------------------------------!!      
           NOTE:
                You can also use the word ALL!
         !!-------------------------------------------------------------!!      

       Restrict Individual Users
       -------------------------

       You may also restrict individual users from any system by 
       creating a file <System # as appears on menu.rst> in the 
       cyber directory.

       example:  

       system.cfg -
                    Circuit Board
                    676-9339
                    20
       1.rst -
                    Joe User
                    John Doe

       In this case any user with a secutity level 20 or higher can
       call Circuit Board. If John Doe or Joe User try they will be
       informed that that system is restricted.


       Adjusting users time by Security Level
       --------------------------------------

       You may find CST to become so popular that users will dial into
       your BBS and just use the Transporter! If this bothers you, then
       you can restrict the time they can use in this door.

       Create a text file called ADJTIME.CFG in the cyber directory. If 
       this file exists it will adjust the users time as indicated in 
       that file. 
       
       format:
       sec level
       max time

       example adjtime.cfg:
       
       255
       60
       
       for all users with secutity level of 255 there time will be adjusted
       to 60 minutes or whatever time they have left. (whichever is less)

       To track the users time for the rest of the day CST will create
       ADJTIME.DAT in the directory it is in. This file MUST be deleted
       as a system event every night!!
       
       Introduction and Exit Screens
       -----------------------------

       If you wish to have introduction and exit screens displayed to the
       users just create:
                  
                 INTRO.ASC            .asc = ascii screens
                 INTRO.ANS
                 EXIT.ASC             .ans = ANSI screens
                 EXIT.ANS


       Custom Menus
       ------------

       CyberSpace Transporter has it's own internal menu's. You can
       create your own ACSII and ANSI menus and CST will use them
       if they exist. If CST cannot find any menu it will use it's 
       internal menu.
        
       Create a menu using your ANSI editor or text editor. Name it:

       M####.ANS or M####.ASC
       
       Where #### is the security level of the user. use ".ANS" for
       ANSI menus and ".ASC" for ASCII menus.
       example:
                m1.ans     <-- will display to user with a security level
                               of 1 on your BBS and if he is using ansi
                
                m25000.asc <-- will display to user with a security level  
                               of 25000 on your BBS and if he is NOT 
                               using ANSI

       

       The system numbers you list in your custom menu should reflect
       the position of the system as it is in SYSTEM.CFG. (or in the
       internal menu) 

       Also the commands Q to quit and E to enter any phone number 
       should be placed in your menu.

       If any menu is not found in the cyber directory, CST will
       use it's own internal menu's.

       
       7E1 Suppport
       ------------

       If the system you are connecting to is at 7E1 (7 bit word - even
       parity - 1 stop bit) then you will need to add "7E1" (without
       the quotes) to the beginning of the number in SYSTEM.CFG.

         !!-------------------------------------------------------------!!      
           NOTE:
                This may be the case for many Unix based systems, some 
                Internet providers, and some networks.
         !!-------------------------------------------------------------!!      

       example system.cfg:

       Real Cool Unix Machine    <-- System Name
       7E1555-1212               <-- number preceeded by 7E1
       10                        <-- security level

       If you also have special modem commands in the phone number string,
       the 7E1 MUST be the first 3 characters.

       The user should not have to set his terminal to 7E1, as they will
       be converted to 8N1.

       
       Trial Accounts
       --------------

       You may charge for or require something from a user to access
       the Transporter on your BBS. In this case you may want to be able
       to offer a free trial. 
       
       CST will read TRIAL.DAT for the users name and date. If the date 
       has not passed then the users security level will be adjusted to 
       the security level specified in the first line of CYBER.CFG. This
       adjustment is only in effect in CyberSpace Transporter and will not
       change the users security level in your bbs userfiles.

       example trial.dat

       Jim Decatur
       10-10-1994
       Joe User
       01-01-1994

       In the above examples Jim Decatur will have his security level 
       raised to the value of the first line of your CYBER.CFG until
       10-10-94. On that date he will have his usual security level
       while in CST. Joe User will have his sl raised until 01-01-94

       NOTE THE FORMAT of the date in trial.dat   MM-DD-YYYY

       
       2.3 Do I really need to get another phone line?
       ====================================================================
       
          NO! 
          
          The Transporter shares my voice line on The Circuit board.

          When the Transporter attempts to dial out if the modem reports
          NO CARRIER the user will be informed the phone line is in
          use and the program will terminate. No different than someone
          picking up an extention in your home. 

          If your BBS is very busy you may want to look into a dedicated
          phone line or restricting the door to certian hours. CST is 
          easy to close as an event. Just create a file called NOT.NOW
          in the cyber directory (contents not important) [see above]

       
       Local Screen
       ====================================================================

          During a transport the local screen will display exactly what
          the user see's. The local screen is live! If you press a key while
          the user is online with another BBS, whatever you press will
          be echo'ed as if the user press the same key on his/her end.
         
         !!-------------------------------------------------------------!!      
           NOTE:
                CST is NOT a terminal program! It will NOT emulate
                ANSI, VT100 or anything while being used locally!
         !!-------------------------------------------------------------!!      
         
          If/when the user downloads a file from the other BBS the screen
          will display the download while it is in progress. This will
          appear as a never ending screen of garbage. Because most downloads
          are of binary files, they will contain "CTRL-G" (BELL) 
          characters. To preserve your sanity all "CTRL-G" characters are
          not printed to the local screen.

          Any time Sysop may press the F1 key. This will terminate 
          CyberSpace Transporter and put the user back in your BBS. 

          A User may also type "EXITCST" if he\she gets stuck on a system.
          This will hang up the dial-out modem and return the user to the 
          CST menu. You may want to inform the user of this command in an
          intro or custom menu screen.

          During transport the Sysop may press the F10 key to toggle on/off
          the status line display. You may want to turn it off after reading 
          the information displayed as it may tend to slow things down.

       Users Time Left
       ====================================================================
       
          CyberSpace Transporter will keep track of the users time left 
          and terminate when his/her time runs out. 
          
          If you have enabled the Hangup feature this will happen during
          a transport. The user will see a warning 2 minutes before
          his time expires.
         
         !!-------------------------------------------------------------!!      
           NOTE:
                If users are paying you per hour, I cannot see any
                reason why you would ever want to hang up on them!!
         !!-------------------------------------------------------------!!      

          If you have not enabled the Hangup feature. Time left will only 
          be enforced at the Transporter Menu screen. If a user runs
          out of time during a transport the program will not terminate
          until s/he returns from a transport.
          


       Registration Information
       ====================================================================

       CyberSpace Transporter (Full Edition) can be used to access ANY
       BBS, on-line service (check their rules), or modem from your BBS.
       255 systems can be configured. CyberSpace Transporter (Full Edition) 
       display's the CyberSpace Transporter copyright screen to your users.

       CST.ZIP is available on The Circuit Board or via Fido Freq at
       1:268/348.
        
       CyberSpace Internet Transporter is for use in accessing an Internet
       provider only. (1 dialout # only) CyberSpace Internet Transporter 
       display's the copyright screen only locally so Internet access 
       appear's local to your BBS.
       
       CyberSpace Internet Transporter                    $35.00
       CyberSpace Transporter (Full Edition)              $45.00

       CyberSpace Transporter (Both Edition's)            $70.00



          If you find this program useful after using it for NO
          LONGER than 30 days. Please send $45.00 to:

          Frances Decatur
          RR 1 Box 59-Q
          Greentown, PA 18426

          Please use ORDER.FRM included in this package.

         !!-------------------------------------------------------------!!      
           Online registration with your Credit Card via modem at:

           The Circuit Board   717-676-9339  (Main support BBS)
           Midnite Connection  718-357-0429
         !!-------------------------------------------------------------!!      

          Any one of you users could save more than the $45.00 in 
          a single month. If you think this is too much, ask your
          users to adopt it!
          
          I will then send you a key to activate this and all future 
          versions of CyberSpace Transporter via FILE ATTACHED EMAIL 
          on The Circuit Board, FIDO CrashMail, Compuserve Email, or 
          call your BBS if there is no other way.
          
          If you want it mailed please include an extra $2.50
          Please indicate 5.25 or 3.5 floppy

          If you do not register CyberSpace Transporter after using it
          for 30 days, destroy your copy or pass it on to someone that
          will!! 

          This offer can be withdrawn at any time! So do it now! Before
          I wake up and charge what it's really worth.