******************** EXPANDED AND EXTENDED MEMORY **************************

ASMLIB's EMS subroutines detect and manipulate Expanded Memory hardware
and software.  Expanded memory, when installed in any PC, can help solve
many memory limitation problems.  Call IsEMS before using any other
ASMLIB EMS subroutines.  All ASMLIB EMS subroutines assume DS:@data.

EMS memory is allocated in blocks of 16k increments

Error codes returned by EMS functions are:

   AH = 0      no error
   AH = 80h    error in memory manager software
   AH = 81h    error in expanded memory hardware
   AH = 84h    bad function code passed to memory manager
   AH = 85h    no EMM handles available
   AH = 89h    you tried to allocate zero pages


ASMLIB also supports XMS-compatible extended memory.  You must call IsXMS
to determine if XMS memory is available before using any ASMLIB XMS
subroutines.  All ASMLIB XMS subroutines assume DS:@data.

XMS memory is available on many 286 or better computers with a suitable
driver.  On 286 computers, XMS memory will be much slower than EMS memory.
XMS memory is not available on XT (or compatible) computers.

XMS memory is allocated in 1k increments

XMS error codes include:

   AH = 0                 no error
   AH = 0A0h              all extended memory is allocated
   AH = 0A1h              no handles available
   AH = 0A2h, 0A3h, 0A5h  handle is invalid
   AH = 0A4h, 0A6h        offset is invalid
   AH = 0A7h              length is invalid


ASMLIB includes disk-based Virtual Memory subroutines (VMS) which make
possible the use of disk space as though it were RAM.  Error codes returned
by VMS subroutines are DOS error codes.

ASMLIB's EMS, VMS and XMS subroutines were written with identical calling
parameters and identical returned information for comparable subroutines.
For example, AllocEMS and AllocXMS are both called with DX:AX = the number
of bytes requested.



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ALLOCEMS:   allocates EMS memory
Source:     ems.asm

Call with:  DX:AX = number of bytes of memory to allocate

            EMS memory is allocated in 16k blocks.  AllocEMS will allocate
            multiple blocks if nessesary.
            NOTE: You must first use IsEMS to determine if Expanded
            memory is installed.

Returns:    if CF = 0, BX = EMS handle
            if CF = 1, AH = EMS error code
Uses:       AX, BX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ALLOCVMS:   allocates VMS memory
Source:     allocvms.asm

Call with:  DX:AX = bytes of VMS memory to allocate
            DS:[SI] pointing to filename for VMS block
            AllocVMS creates a file of the size requested, thus reserving
            space on the disk for the memory block.  The file should not
            be presumed to contain useful data.
Returns:    if CF = 0, BX = VMS handle
            if CF = 1, AX = DOS error code
Uses:       AX, BX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ALLOCXMS:   allocates XMS memory
Source:     xms.asm

Call with:  DX:AX = number of bytes of memory to allocate

            XMS memory is allocated in 1k blocks.  AllocXMS will allocate
            multiple blocks if nessesary.
            NOTE: You must first use IsXMS to determine if XMS Extended
            memory is available.

Returns:    if CF = 0, BX = XMS handle
            if CF = 1, AH = XMS error code
Uses:       AX, BX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMGET:      copy data from EMS memory to system RAM
Source:     emputget.asm ($emspage.asm)

Call with:  BX = EMS handle
            ES:[DI] pointing to destination buffer
            DS:[SI] pointing to 4-byte offset in EMS block
            DX:AX = number of bytes to copy
Returns:    if CF = 0, no error
            if CF = 1, AH = EMS error code
Uses:       AX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMMOVE:     move data within an EMS memory block
            this is used most often to make room for additional data
            at a specified location in the EMS block, or to delete data
            from the block.
Source:     emmove.asm (xget$.asm, $xmove.asm, emputget.asm, $emspage.asm)

Call with:  BX = valid EMS handle
            DS:[SI] pointing to source offset in EMS block
            DS:[DI] pointing to destination offset in EMS block
            DX:AX = number of bytes to move

            64k DOS memory must be available; assumes DS:@data
            EMMove works properly if the source and destination
            overlap; you must make sure the EMS block is large enough
            to accomodate the move.

Returns:    if CF = 0, no error
            if CF = 1, AH = DOS or EMS error code
               the only DOS error code likely is 08h, insufficient memory

Uses:       AX, flags
Example:

; calculate bytes to move
        mov     ax,block_size
        mov     dx,block_size   ; DX:AX = bytes in expanded memory block
        sub     ax,source
        sbb     dx,source+2     ; DX:AX = bytes in tail end of block
                                ;       = bytes to move
        mov     bx,block_handle
        lea     si,source
        lea     di,destination
        call    emmove




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMMVER:     determines Expanded Memory Manager version
Source:     emmver.asm

Call with:  no parameters
Returns:    if CF = 1, AH = EMS error code
            if CF = 0, AH = major version number
                       AL = minor version number
Uses:       AX, flags
Example:

include  asm.inc

extrn    isems:proc, emmver:proc

.code
         .
         .
         .
         call   isems
         jc     no_ems
         call   emmver     ; get emm version
         jc     ems_error
         cmp    ah,4       ; version 4.x?
         jb     version3x  ; nope, an older EMM version



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMPUT:      copy data to EMS memory from system RAM
Source:     emputget.asm ($emspage.asm)

Call with:  BX = EMS handle
            ES:[DI] pointing to data to copy
            DS:[SI] pointing to 4-byte offset in EMS block
            DX:AX = number of bytes to copy
Returns:    if CF = 0, no error
            if CF = 1, AH = EMS error code
Uses:       AX, flags
Example:    see example code at the end of this file




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMSFREE:    determine free EMS memory
Source:     emsfree.asm

Call with:  no parameters

            EMSFree does not verify that EMS memory is installed; you should
            call IsEMS to determine if EMS memory is installed before using
            this subroutine.  Do not confuse this subroutine with FreeEMS,
            which releases a previously allocated EMS block and handle.

Returns:    DX:AX = bytes of EMS memory available
Uses:       AX, DX, flags
Example:

include asm.inc

public  myprog
extrn   isems:proc, emsfree:proc

.code
myprog  proc
        call    isems           ; see if EMS memory is installed
        jc      nope
        call    emsfree         ; is enough available?
        .
        .
        .



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMSTOTAL:   determine total EMS memory installed
Source:     emsfree.asm

Call with:  no parameters; call IsEMS to determine if EMS memory is
            installed before using this subroutine
Returns:    DX:AX = bytes of EMS memory installed
Uses:       AX, DX, flags
Example:

include asm.inc

public  myprog
extrn   isems:proc, emstotal:proc

.code
myprog  proc
        call    isems           ; see if EMS memory is installed
        jc      nope
        call    emstotal        ; how much?
        .
        .
        .



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EMISTR:     search expanded memory block for ASCIIZ string, case-insensitive
Source:     emistr.asm (xget$.asm, $xistr.asm, emputget.asm, strlen.asm,
                        $strstr.asm, strlwr.asm)

EMSTR:      search expanded memory block for ASCIIZ string, case-sensitive
Source:     emstr.asm (xget$.asm, $xstr.asm, emputget.asm, $strstr.asm,
                       strlen.asm)

Call with:  DS:[SI] pointing to ASCIIZ string
            BX = valid EMS handle
            DS:[DI] pointing to 4-byte initial offset for start of search
            DX:AX = number of bytes of EMS block to search
            requires 64k free DOS memory (see ENDPROG and STARTUP.ASM)

Returns:    if CF = 0, DX:AX = offset of matching string in EMS block
            if CF = 1:
               if AX = 0, string not found
                else AH = EMS error code
Uses:       DX,AX, flags

Example:

include asm.inc

public  mycode
extrn   emstr:proc

.data
extrn   ems_handle:word
extrn   ems_bytes:word          ; 2 words
ems_offset      dw 0,0          ; start at beginnig of block
search_string   db 'ASMLIB',0

.code
mycode  proc
; program fragment assumes EMS memory has been allocated
; and has useful data

        .
        .
        lea     si,search_string
        mov     bx,ems_handle
        mov     ax,ems_bytes
        mov     dx,ems_bytes+2  ; DX:AX = bytes to search
        lea     di,ems_offset   ; start search at beginning of XMS block
        call    emstr           ; returns DX:AX = offset of 'ASMLIB'
        jnc     found_it
        or      ax,ax
        jz      no_match        ; no errors, but no match either
        jmp     oh_no_an_error  ; jump to error handling code




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOADEMS:   reads a disk file and copies to EMS memory
Source:     floadems.asm (fsize.asm, ems.asm)

Call with:  DS:[DX] pointing to ASCIIZ filename
            call IsEMS before calling FLoadEMS to determine if EMS memory
            is available
Returns:    if CF = 0, BX = EMS handle and DX:AX = bytes copied to EMS
            if CF = 1, AH = EMS error code or AL = DOS error code
Uses:       AX, BX, DX, CF
Example:

include asm.inc

public  test_ems

extrn   isems:proc
extrn   gsave:proc, floadems:proc

.data
handle  dw 0
fname   db 'filename.12h',0

.code
test_ems        proc
; program fragment assumes DS:@data
        mov     ax,12h          ; VGA 16-color mode
        int     10h             ; set mode
        .                       ; program draws screen
        .

; I want to save this screen as a disk file
     call isems
     jc   no_good
     lea  dx,fname
     call gsave           ; GSave is in GRAPHICS.DOC
     jc   no_good
        .
        .

; now I want to get back the screen I saved
        lea     dx,fname
        call    floadems        ; read file, load into EMS memory
        mov     handle,bx
        jc      no_good
        call    gloadems        ; copy from EMS memory to video buffer
        jc      kill_ems
        call    getkey          ; now look at the pretty picture
kill_ems:
        mov     dx,handle
        mov     ah,45h
        int     67h

no_good:call    modecolor       ; go back to color text mode
        ret
test_ems        endp
        end


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOADVMS:   reads a disk file and copies to VMS memory
Source:     floadvms.asm (fcopy.asm, fsize.asm)

Call with:  DS:[DX] pointing to input ASCIIZ filename
            DS:[SI] pointing to VMS filename
             The VMS filename is the name of the file created as VMS memory
             64k DOS memory must be available for FLoadVMS' use

Returns:    if CF = 0, BX = VMS handle and DX:AX = bytes copied
            if CF = 1, AX = DOS error code
Uses:       AX, BX, DX, flags
Example:    see FLoadEMS example



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOADXMS:   reads a disk file and copies to XMS memory
Source:     floadxms.asm (fsize.asm, xmputget.asm, xms.asm)

Call with:  DS:[DX] pointing to ASCIIZ filename
            call IsXMS before calling FLoadXMS to determine if XMS memory
            is available

            64k DOS memory must be available for FLoadXMS' use

Returns:    if CF = 0, BX = XMS handle and DX:AX = bytes copied to XMS
            if CF = 1, AH = XMS error code or AL = DOS error code
Uses:       AX, BX, DX, CF
Example:    see FLoadEMS example



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FSAVEEMS:   writes an EMS memory block to disk file
Source:     fsaveems.asm ($fsavex.asm, emputget.asm)

Call with:  DS:[SI] pointing to ASCIIZ filename
            BX = valid EMS handle
            DX:AX = bytes to write

            64k DOS memory must be available for FSaveEMS' use

Returns:    if CF = 0, no error
            if CF = 1, AH = EMS error code or AL = DOS error code
Uses:       AX, flags
Example:

.data
emsfile        db 'bigblock.ems',0
emssize        dd ?                  ; program fills in the numbers
emshandle      dw ?                  ; program fills in the numbers

.code
swap_ems_to_disk   proc
; program fragment assumes DS:@data
       lea     si,emsfile            ; filename
       mov     bx,emshandle
       mov     ax,word ptr emssize
       mov     dx,word ptr emssize+2 ; DX:AX = bytes to save
       call    fsaveems              ; save EMS block as disk file
       jc      no_good



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FSAVEVMS:   save a VMS memory block as a disk file
Source:     fsavevms.asm (xget$.asm, $fsavex.asm, vmputget.asm)

Call with:  DS:[SI] pointing to ASCIIZ filename
            BX = valid VMS handle
            DX:AX = bytes to write

            64k DOS memory must be available for FSaveVMS' use

Returns:    if CF = 0, no error
            if CF = 1, AX = DOS error code
Uses:       AX, flags
Example:    see FSaveEMS example




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FSAVEXMS:   writes an XMS memory block to disk file
Source:     fsavexms.asm (xget$.asm, $fsavex.asm, xms.asm, xmputget.asm)

Call with:  DS:[SI] pointing to ASCIIZ filename
            BX = valid XMS handle
            DX:AX = bytes to write

            64k DOS memory must be available for FSaveXMS' use

Returns:    if CF = 0, no error
            if CF = 1, AH = XMS error code or AL = DOS error code
Uses:       AX, flags
Example:    see FSaveEMS example



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FREEEMS:    releases an EMS memory block and handle
Source:     ems.asm

Call with:  BX = EMS handle

            NOTE: DOS does not release EMS memory when your program
            returns to DOS.  Your program must close any open EMS handles
            before quitting, or the EMS memory associated with the handles
            will be unavailable to other programs.  Do not confuse this
            subroutine with EMSFree, whick determines the EMS memory
            available.

Returns:    if CF = 0, no error
            if CF = 1, AH = EMS error code
Uses:       AX, flags
Example:    see example code at the end of this file




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FREEVMS:    releases a VMS memory block and handle
Source:     freevms.asm

Call with:  BX = VMS handle
            DS:[SI] pointing to VMS block filename

Returns:    if CF = 0, no error
            if CF = 1, AX = DOS error code
Uses:       AX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FREEXMS:    releases an XMS memory block and handle
Source:     xms.asm

Call with:  BX = XMS handle

            NOTE: DOS does not release XMS memory when your program ends.
            Your program must close any open XMS handles before quitting,
            or the XMS memory associated with the handles will be
            unavailable to other programs.  Do not confuse this subroutine
            with XMSFree, whick determines the XMS memory available.

Returns:    if CF = 0, no error
            if CF = 1, AH = XMS error code
Uses:       AX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISEMS:      detects EMS driver
Source:     isems.asm

Call with:  no parameters
Returns:    if CF = 1, no Expanded Memory manager installed
            if CF = 0, EMS memory is installed
Uses:       CF
Example:    see example code at the end of this file





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISXMS:      detects XMS driver
Source:     isxms.asm
Call with:  no parameters
Returns:    if CF = 1, no XMS driver is installed
            if CF = 0, XMS memory is available
Uses:       CF
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

REALLOCEMS: re-size a previously allocated EMS memory block
Source:     realloce.asm

Call with:  BX = valid EMS memory handle
            DX:AX = requested bytes
Returns:    if CF = 0, no error
            if CF = 1, AH = EMS error code
Supports:   EMS version 4.0 or greater (see EMMVER)
Uses:       AX, flags
Example:

        mov   bx,emshandle           ; existing valid EMS handle
        mov   ax,bytes
        mov   dx,bytes+2             ; DX:AX = bytes requested
        call  reallocems             ; try to re-size existing block
        jc    alloc_error


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

REALLOCVMS: re-size a previously allocated VMS memory block
Source:     reallocv.asm

Call with:  BX = valid VMS memory handle
            DX:AX = requested bytes

            Note that ReallocVMS can only make the VMS block larger
            if a smaller VMS block is requested, ReallocVMS does nothing
            and returns with CF = 0

Returns:    if CF = 0, no error
            if CF = 1, AX = DOS error code
Uses:       AX, flags
Example:

        mov   bx,vmshandle           ; existing valid VMS handle
        mov   ax,bytes
        mov   dx,bytes+2             ; DX:AX = bytes requested
        call  reallocvms             ; try to re-size existing block
        jc    alloc_error



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

REALLOCXMS: re-size a previously allocated XMS memory block
Source:     reallocx.asm (xms.asm)

Call with:  BX = valid XMS memory handle
            DX:AX = requested bytes
Returns:    if CF = 0, no error
            if CF = 1, AH = XMS error code
Uses:       AX, flags
Example:

        mov   bx,xmshandle           ; existing valid XMS handle
        mov   ax,bytes
        mov   dx,bytes+2             ; DX:AX = bytes requested
        call  reallocxms             ; try to re-size existing block
        jc    alloc_error


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VMGET:      copy data from VMS memory to system RAM
Source:     vmputget.asm

Call with:  BX = VMS handle
            ES:[DI] pointing to destination buffer
            DS:[SI] pointing to 4-byte offset in VMS block
            DX:AX = number of bytes to copy
Returns:    if CF = 0, no error
            if CF = 1, AX = DOS error code
Uses:       AX, flags
Example:    see example code at the end of this file




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VMMOVE:     move data within a VMS memory block
Source:     vmmove.asm (xget$.asm, $xmove.asm, vmputget.asm)

Call with:  BX = valid VMS handle
            DS:[SI] pointing to source offset in VMS block
            DS:[DI] pointing to destination offset in VMS block
            DX:AX = number of bytes to move

            64k DOS memory must be available; assumes DS:@data
            VMMove works properly if the source and destination
            overlap; you must make sure the block is large enough
            to accomodate the move.

Returns:    if CF = 0, no error
            if CF = 1, AX = DOS error code

Uses:       AX, flags
Example:

; calculate bytes to move
        mov     ax,block_size
        mov     dx,block_size   ; DX:AX = bytes in extended memory block
        sub     ax,source
        sbb     dx,source+2     ; DX:AX = bytes in tail end of block
                                ;       = bytes to move
        mov     bx,block_handle
        lea     si,source
        lea     di,destination
        call    vmmove


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VMPUT:      copy data to VMS memory from system RAM
Source:     vmputget.asm

Call with:  BX = VMS handle
            ES:[DI] pointing to data to copy
            DS:[SI] pointing to 4-byte offset in VMS block
            DX:AX = number of bytes to copy
Returns:    if CF = 0, no error
            if CF = 1, AX = VMS error code
Uses:       AX, flags
Example:    see example code at the end of this file





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VMISTR:     search VMS memory block for ASCIIZ string, case-insensitive
Source:     vmistr.asm (xget$.asm, $xistr.asm, vmputget.asm, strlen.asm,
                        strlwr.asm)

VMSTR:      search VMS memory block for ASCIIZ string, case-sensitive
Source:     vmstr.asm (xget$.asm, $xstr.asm, vmputget.asm, strlen.asm)

Call with:  DS:[SI] pointing to ASCIIZ string
            BX = valid VMS handle
            DS:[DI] pointing to 4-byte initial offset for start of search
            DX:AX = number of bytes of VMS block to search
            requires 64k free DOS memory (see ENDPROG and STARTUP.ASM)

Returns:    if CF = 0, DX:AX = offset of matching string in VMS block
            if CF = 1:
               if AX = 0, string not found
                else AX = DOS error code
Uses:       DX, AX, flags

Example:

include asm.inc

public  mycode
extrn   vmstr:proc

.data
extrn   vms_handle:word
extrn   vms_bytes:word          ; 2 words
vms_offset      dw 0,0          ; start at beginnig of block
search_string   db 'ASMLIB',0

.code
mycode  proc
; program fragment assumes VMS memory has been allocated
; and has useful data

        .
        .
        lea     si,search_string
        mov     bx,vms_handle
        mov     ax,vms_bytes
        mov     dx,vms_bytes+2  ; DX:AX = bytes to search
        lea     di,vms_offset   ; start search at beginning of VMS block
        call    vmstr           ; returns DX:AX = offset of 'ASMLIB'
        jnc     found_it
        or      ax,ax
        jz      no_match        ; no errors, but no match either
        jmp     oh_no_an_error  ; jump to error handling code




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

XMGET:      copy data from XMS memory to system RAM
Source:     xmputget.asm (xms.asm)

Call with:  BX = XMS handle
            ES:[DI] pointing to destination buffer
            DS:[SI] pointing to 4-byte offset in XMS block
            DX:AX = number of bytes to copy (minimum 2 bytes)
Returns:    if CF = 0, no error
            if CF = 1, AH = XMS error code
Uses:       AX, flags
Example:    see example code at the end of this file



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

XMMOVE:     move data within an XMS memory block
Source:     xmmove.asm (xget$.asm, $xmove.asm, xmputget.asm, xms.asm)

Call with:  BX = valid XMS handle
            DS:[SI] pointing to source offset in XMS block
            DS:[DI] pointing to destination offset in XMS block
            DX:AX = number of bytes to move (minimum 2 bytes)

            64k DOS memory must be available; assumes DS:@data
            XMMove works properly if the source and destination
            overlap; you must make sure the block is large enough
            to accomodate the move.

Returns:    if CF = 0, no error
            if CF = 1, AH = DOS or XMS error code
               the only DOS error code likely is 08h, insufficient memory

Uses:       AX, flags
Example:

; calculate bytes to move
        mov     ax,block_size
        mov     dx,block_size   ; DX:AX = bytes in extended memory block
        sub     ax,source
        sbb     dx,source+2     ; DX:AX = bytes in tail end of block
                                ;       = bytes to move
        mov     bx,block_handle
        lea     si,source
        lea     di,destination
        call    xmmove




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

XMPUT:      copy data to XMS memory from system RAM
Source:     xmputget.asm (xms.asm)

Call with:  BX = XMS handle
            ES:[DI] pointing to data to copy
            DS:[SI] pointing to 4-byte offset in XMS block
            DX:AX = number of bytes to copy (minimum 2 bytes)
Returns:    if CF = 0, no error
            if CF = 1, AH = XMS error code
Uses:       AX, flags
Example:    see example code at the end of this file




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

XMSFREE:    determine free XMS memory
Source:     xmsfree.asm

Call with:  no parameters

            XMSFree does not verify that XMS memory is installed; you should
            call IsXMS to determine if XMS memory is installed before using
            this subroutine.  Do not confuse this subroutine with FreeXMS,
            which releases a previously allocated XMS block and handle.

Returns:    DX:AX = bytes of XMS memory available
Uses:       AX, DX, flags
Example:

include asm.inc

public  myprog
extrn   isxms:proc, xmsfree:proc

.code
myprog  proc
        call    isxms           ; see if XMS memory is installed
        jc      nope
        call    xmsfree         ; is enough available?
        .
        .
        .




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

XMISTR:     search extended memory block for ASCIIZ string, case-insensitive
Source:     xmistr.asm (xget$.asm, $xistr.asm, xmputget.asm, strlen.asm,
                        strlwr.asm)

XMSTR:      search extended memory block for ASCIIZ string, case-sensitive
Source:     xmstr.asm (xget$.asm, $xstr.asm, xmputget.asm, strlen.asm)

Call with:  DS:[SI] pointing to ASCIIZ string
            BX = valid XMS handle
            DS:[DI] pointing to 4-byte initial offset for start of search
            DX:AX = number of bytes of XMS block to search
            requires 64k free DOS memory (see ENDPROG and STARTUP.ASM)

Returns:    if CF = 0, DX:AX = offset of matching string in XMS block
            if CF = 1:
               if AX = 0, string not found
                else AH = XMS error code
Uses:       DX,AX, flags

Example:

include asm.inc

public  mycode
extrn   xmstr:proc

.data
extrn   xms_handle:word
extrn   xms_bytes:word          ; 2 words
xms_offset      dw 0,0          ; start at beginnig of block
search_string   db 'ASMLIB',0

.code
mycode  proc
; program fragment assumes XMS memory has been allocated
; and has useful data

        .
        .
        lea     si,search_string
        mov     bx,xms_handle
        mov     ax,xms_bytes
        mov     dx,xms_bytes+2  ; DX:AX = bytes to search
        lea     di,xms_offset   ; start search at beginning of XMS block
        call    xmstr           ; returns DX:AX = offset of 'ASMLIB'
        jnc     found_it
        or      ax,ax
        jz      no_match        ; no errors, but no match either
        jmp     oh_no_an_error  ; jump to error handling code






; EXPANDED AND EXTENDED MEMORY EXAMPLE CODE

; This example determines if EMS or XMS memory is installed, allocates
; 32k of EMS or XMS memory, copies a Herules graph to the allocated memory
; and later, copies the data back to the video buffer and releases
; the memory block

include asm.inc

public  herc2x

extrn   isems:proc, isxms:proc
extrn   allocems:proc, allocxms:proc
extrn   emput:proc, xmput:proc
extrn   emget:proc, xmget:proc
extrn   freeems:proc, freexms:proc

.data
IF @codesize
xalloc  dd 0
xput    dd 0
xget    dd 0
xfree   dd 0
ELSE
xalloc  dw 0
xput    dw 0
xget    dw 0
xfree   dw 0
ENDIF
xoffset dw 0,0
xhandle dw 0
xerror  dw 0

.code
herc2x  proc
; program fragment assumes DS:@data
; set up default conditions: use EMS
        mov     xerror,offset ems_error
        mov     word ptr xalloc,offset allocems
        mov     word ptr xput,offset emput
        mov     word ptr xget,offset emget
        mov     word ptr xfree,offset freeems
IF @codesize
        mov     ax,seg allocems
        mov     word ptr xalloc+2,ax  ; all ASMLIB code in same segment
        mov     word ptr xput+2,ax
        mov     word ptr xget+2,ax
        mov     word ptr xfree+2,ax
ENDIF


; see if EMS is installed
        call    isems
        jnc     allocate_memory

; EMS not installed - see if XMS memory is avaialble
; set up for XMS subroutines
        mov     xerror,offset xms_error
        mov     word ptr xalloc,offset allocxms
        mov     word ptr xput,offset xmput
        mov     word ptr xget,offset xmget
        mov     word ptr xfree,offset freexms
IF @codesize
        mov     ax,seg allocxms
        mov     word ptr xalloc+2,ax  ; all ASMLIB code in same segment
        mov     word ptr xput+2,ax
        mov     word ptr xget+2,ax
        mov     word ptr xfree+2,ax
ENDIF
        call    isxms
        jc      foiled_again         ; don't use EMS or XMS

; allocate 32k
allocate_memory:
        mov     ax,32768
        xor     dx,dx                ; DX:AX = 32768
        call    xalloc               ; allocate EMS or XMS memory block
        jc      xerror
        mov     xhandle,bx           ; save the handle

; copy the graph to EMS or XMS
        mov     di,0B000h            ; Hercules buffer
        mov     es,di
        xor     di,di                ; ES:[DI] -> video buffer
        mov     ax,32768             ; copy entire graph
        lea     si,xoffset           ; start at offset 0 in memory block
        call    xput                 ; copy the graph to memory
        jc      xerror

; later ...
; copy the graph back to the video buffer
        mov     bx,xhandle
        mov     dx,0B000h
        mov     es,dx
        xor     di,di                ; ES:[DI] points to destination
        mov     ax,32768             ; copy all 32k
        xor     dx,dx                ; DX:AX = 32768
        lea     si,xoffset           ; start at offset 0 in memory block
        call    xget                 ; copy the graph back to video buffer
        jc      xerror

; all done with graph copy; release the memory block
        call    xfree
        jc      xerror