ÜÜÜÜÜÜÜ  ÜÜÜ
               °°°°°°°  °°°
                °°   °   °°    ÜÜÜÜ  ÜÜ ÜÜÜ  ÜÜ ÜÜÜ  ÜÜ  ÜÜ
                °°ÜÜ     °°   Ü°°°°Ü °°Ü°°°Ü °°Ü°°°Ü °°  °°
                °°°°     °°   °°  °°  °°  °°  °°  °° °°  °°
                °°       °°   °°  °°  °°ÜÜ°°  °°ÜÜ°° °°ÜÜ°°
               Ü°°Ü      °°Ü  °°ÜÜ°°  °°°°°   °°°°°   °°°°°
               °°°°      °°°   °°°°  Ü°°     Ü°°      ÜÜÜ°°
                                     °°°     °°°      °°°°°

                                ÜÜÜÜÜÜ                  ÜÜÜ
                                °°°°°°                  °°°
                                ° °° °   ÜÜÜÜ    ÜÜÜÜ    °°
                                  °°    Ü°°°°Ü  Ü°°°°Ü   °°
                                  °°    °°  °°  °°  °°   °°
                                  °°    °°  °°  °°  °°   °°
                                 Ü°°Ü   °°ÜÜ°°  °°ÜÜ°°   °°Ü
                                 °°°°    °°°°    °°°°    °°°

                                         ÜÜÜ  ÜÜ   ÜÜ     Ü
                                         °°°  °°   °°    Ü°
                                          °° Ü°°  ÜÜÜ   Ü°°Ü
                                          °°Ü°°   °°°   °°°°
                                          °°°°     °°    °°
                                          °°°°Ü    °°    °° Ü
                                         Ü°° °°Ü   °°Ü   °°Ü°
                                         °°°  °°   °°°    °°

                                             ÜÜ          ÜÜ
                                            Ü°°         Ü°°
                                            °°°         °°°
                                             °°          °°
                                             °°          °°
                                             °°    ÜÜ    °°
                                           ÜÜ°°ÜÜ  °°  ÜÜ°°ÜÜ
                                           °°°°°°  °°  °°°°°°


                                              William Luitje
                                               13 March 1995

        This is a collection of 8 small utilities which will help you use 
        your  floppy  disks more effectively.   Since you probably  worry 
        more  about  how to get better speed and storage out of your hard 
        disk,   this  may  not  be a matter of pressing concern  to  you.  
        However,  floppies are going to be used for quite a while and  by 
        spending  a few minutes with these utilities you can make  things 
        go a  little bit faster each time you use a floppy.  Programs are 
        provided to 

          þ set the mechanical parameters of operation for your floppies

          þ test for the maximum reliable step rate of a floppy drive

          þ test a drive or disk for read errors

          þ measure the seek performance of a floppy system

          þ determine the optimal skewing parameters for formatting disks

          þ test the rotational speed of a drive for accuracy

          þ show the formatting parameters for a floppy disk

          þ aid in the use of a head cleaning disk

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± FLOPPARM ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Floppies  have  been  around a long time and have  been  improved 
        since they first came out, not only in capacity but also in their 
        mechanical  speed and  accuracy.  Unfortunately,  system software 
        can't tell what the  best speed to drive a floppy is and must  be 
        compatible  with  old  drives  and  so uses  conservatively  slow 
        parameters.    When  accessing  a  floppy,  the BIOS uses a table 
        called  the  Diskette  Parameter  Table  for  these   parameters.  
        Interrupt vector 1E contains the address of this table.  Since it 
        is  usually  set up in RAM by DOS,  it is easy to modify  it  for 
        modern, fast drives.  FLOPPARM will do this for you conveniently; 
        simply run it  with one of the three arguments SLOW,  MEDIUM,  or 
        FAST.  The parameters which are affected are: 

          þ step  rate and head unload time, which  are parameters of the 
            disk controller chip. 

          þ head settle time,  which is the amount of time the BIOS takes 
            after stepping from one track to another to wait for the head 
            mechanism to stop vibrating. 

          þ motor startup time,  which is the amount of time taken by the 
            BIOS  to allow the spindle motor speed to stabilize after  it 
            first starts up. 

        SLOW is provided for compatibility with really old drives; MEDIUM 
        is somewhat faster than DOS 5;  and FAST is pedal to metal!  When 
        run, FLOPPARM displays the parameters used.  If run with no or an 
        illegal  argument,   FLOPPARM will display a usage hint  and  the 
        current values of the parameters. 

        FLOPPARM also allows you to specify your own parameters by  using 
        the  CUSTOM  argument  followed by an equals sign  and  the  four 
        parameters  (step rate,  head unload time,  head settle time  and 
        motor startup time) separated by commas (no spaces allowed).  For 
        example a command equivalent to FLOPPARM MEDIUM would be 

        flopparm custom=13,15,1,2 

        Legal values for step rate and head unload time are from 1 to 15.  
        Legal values for head  settle  time  (in milliseconds)  and motor 
        startup time (in 1/8s of a second) are from 1 to 255.  
        
        How do you decide what custom values to use?  Obviously, to speed 
        up  operation,  increase step rate and decrease head unload time, 
        head  settle  time and motor startup time.   Since motor  startup 
        time is given in eighths of a second and the other parameters are 
        given  in milliseconds,  it seems like a good place to look for a 
        speed increase.   I've had no problems setting it to one and that 
        produces  a noticeable reduction in the time you have to wait for 
        the floppy when the motor is off. 

        I've  provided two utilities to help in testing your settings for 
        the rest of the parameters, TESTSTEP and FLOPTEST.  These will be 
        described in subsequent sections.   In any case,  once you decide 
        which  parameters to use,  just put a line invoking  FLOPPARM  in 
        your  AUTOEXEC.BAT  file  and enjoy a modest increase  in  floppy 
        speed. 
        
        NOTES: FLOPPARM is not a TSR and does not take up any DOS memory; 
        it  simply  modifies  a table in RAM which is already  created by 
        DOS.   Also,  there is only one table to control the operation of 
        all  of  the  floppy drives in your system;  make  sure that your 
        slowest drive can handle the parameters you set. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± TESTSTEP ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Use TESTSTEP to find the fastest step rate which can be used with 
        a  particular floppy drive.  It starts with the highest  possible 
        step  rate,   15,  and then does a large number of seeks  on  the 
        selected drive to see if that rate is too fast.   If so, then the 
        step  rate is lowered and the test retried until all of the seeks 
        can be done without error. 

        To run this test you must use  a floppy  which has been formatted 
        with no errors at the standard size for that drive.  For example, 
        if  you are testing a 5¬"  High Density drive you must use a  1.2 
        Meg disk,  not a 360K disk.  Similarly,  you shouldn't use a 720K 
        disk in a 3«" High Density drive or vice versa. 

        This  test appears to be very stringent;  no drive which  I  have 
        tested  has  passed it with a step rate of 15.   However,  during 
        normal  use  most floppies seem to work at that  rate,   probably 
        because the seeks are not as severe.   You can be sure that if it 
        passes this test it will work reliably during normal use. 

        Note that this program by doesn't test the head unload  and  head 
        settle  times  at  all.   You can test these indirectly with  the 
        FLOPTEST utility described in the next section. 

        TESTSTEP takes one argument,  the drive letter.  Only A and B are 
        supported at this time.  Here is an example command and result. 

          teststep b

          Test Maximum Floppy Step Rate, Ver 1.0 by luitje@m-net.arbornet.org

          Drive B: has 80 tracks; current Step Rate is 13

          Testing Step Rate = 15:  failed
          Testing Step Rate = 14:  failed
          Testing Step Rate = 13:  passed

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± FLOPTEST ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        FLOPTEST  provides a practical test of whether you have set  your 
        floppy  drive parameters too fast.   It will simply seek to every 
        track of the disk,  read a sector and report any errors it finds.  
        The seek pattern is called a "butterfly test"  since it reads the 
        first track, then the last track, then the second track, then the 
        next  to  last track,  etc.   This will really give the  drive  a 
        workout! 

        This test requires a formatted floppy which has no  bad  sectors. 
        (FLOPTEST  can't tell if an error is due to the drive not working 
        properly  or  due to a bad disk).   It is a read only test so  it 
        shouldn't change any data on the disk.  There are two parameters: 
        one is the drive letter and the second is the number of passes to 
        run.  If you get any errors and your floppy is ok then you should 
        back  off  one or more of the floppy drive  parameters  and  test 
        again. Here is an example 

          floptest a 20 

        If you are fortunate enough to have more than 2 disk drives (this 
        applies  both  to  FLOPTEST and to the other  utilities  in  this 
        package, except where noted), you can refer to the third drive as 
        c and the  fourth drive as d,  even if you have a hard drive that 
        goes by either of those names.  I know this is confusing but this 
        test operates at the  BIOS  level and has no idea what letter DOS 
        has assigned to your third and fourth floppies.   I  had a choice 
        of  confusing  people  who  had  more than  2  floppy  drives  or 
        confusing everybody by making you specify the drive with a number 
        rather than a letter.  That's life. 

        You  can  also use FLOPTEST to see if a floppy disk has  any  bad 
        sectors.    If  you run it with only the drive letter  specified, 
        then  it will attempt to read every sector  (linearly,   starting 
        with track 0) and report any failures.  Since FLOPTEST makes only 
        one attempt to read each sector,  it will warn you if a sector is 
        getting  weak.   I  use this feature a lot before putting any new 
        information  on an old disk.   If the disk has errors,  I  either 
        reformat it or throw it away. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± SEEKBNCH ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Once  you have your parameters set as you like them you  can  use 
        SEEKBNCH  to  measure  how fast your drive  will  seek  with  the 
        controller  set  to  the  current  step  rate parameter. SEEKBNCH 
        performs three benchmarks: 

          þ track to track seek time

          þ average seek time

          þ full stroke seek time

        The  step  rate should be set either by default or  via  FLOPPARM 
        before this test is run (head settle time is ignored).   However, 
        do  not use a step rate faster than that passed by TESTSTEP.   At 
        best  the  results  will be meaningless and at  worst  you  might 
        damage your drive. 
        
        To  run  the  benchmark  you will need  an  error-free  formatted 
        floppy.  SEEKBNCH takes one parameter,  the drive letter (only  A 
        and B are supported).  Here's a sample command and sample output. 

          seekbnch a

          Floppy Disk Seek Benchmark, Ver 1.0 by luitje@m-net.arbornet.org

          Drive A: has 80 tracks; current Step Rate is 14

          Track to track seek time:   3.0 mSecs
          Average seek time:         81.7 mSecs
          Full Stroke seek time:    309.5 mSecs

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± FLOPSKEW ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The most important improvement you can make in using your  floppy 
        drives  is  to  format  your disks using  FDFORMAT  by  Christoph 
        Hochst„tter or  ATFMT by Oleg Kibirev.   They can be found on the 
        Internet   in  any  of  the  SimTel  archives  in  the  directory 
        msdos/diskutil. These programs allow almost complete control over 
        how your disks are formatted.  Among other things, you can put up 
        to 820K on 5¬" DSDD disks, 1.48 meg on 5¬"  HD disks and 1.7  meg 
        on 3«" HD disks.   In terms of speeding up floppy disk transfers, 
        these programs allow you  to control the way sectors are arranged 
        on  a track.   This concept is called  sector sliding by FDFORMAT 
        and  sector  spinning by ATFMT;  in the US it's known  as  sector 
        skewing.    Basically,   the  idea is that since  there  is  some 
        mechanical delay in changing heads  or tracks it may be desirable 
        to put the first sector of a new  head or track  "later"   in the 
        track so the computer doesn't have to wait for the floppy to make 
        a complete revolution before that sector can be read.   See these 
        programs' documentation for more details on how this works.   The 
        time savings when  reading or writing a floppy can be substantial 
        when you format it using  the optimal skew parameters and,  as an 
        added benefit, formatting is faster, too. 

        You  can  specify head skew and track skew in both  FDFORMAT  and 
        ATFMT by the X and Y parameters,  respectively.   The DOS  FORMAT 
        program  does  not  support  sector  skewing  at  all;   this  is 
        equivalent  to  using FDFORMAT or ATFMT with X and Y both set  to 
        zero.    But  what  values should you use for  these  parameters?  
        Well,   when FDFORMAT first introduced this feature,  I  wrote  a 
        batch file which formatted a test disk with various  combinations 
        of the head and sector skew parameters and then measured how long 
        it  took  to copy a large file to the floppy.   It took about  an 
        hour to run and tested 16 combinations of X and Y values for just 
        one  disk  format.    FLOPSKEW does the same job in  just  a  few 
        seconds but tests even more combinations of parameter values. 
        
        To  use FLOPSKEW,  first decide which setting of FLOPPARM to  use 
        and then run FLOPPARM with that parameter since the step rate and 
        head settle time will both affect skewing.   Then,  format a disk 
        of  the type and capacity for which you want to find the  optimal 
        skewing  parameters  with  the  X and Y  parameters  both  0  and 
        interleave 1.   Although FLOPSKEW is a non-destructive test,  you 
        should  use  a  freshly  formatted  disk  to  ensure  that  these 
        parameters  are  set  correctly,  otherwise the  test  will  give 
        strange  results.    If you don't specify X and Y,  FDFORMAT  and 
        ATFMT  default to the correct values except that they  both  must 
        use  an interleave of 2 for the 5¬"  1.44  meg and 3«"  1.7   meg 
        formats  (and for this reason it doesn't make sense to use sector 
        skewing  with these formats).  DOS FORMAT always formats with  no 
        sector skewing and interleave 1. 

        Then, simply run FLOPSKEW with the drive letter of the floppy you 
        want to test as the only parameter.   Here is an example  command 
        and  its  results  for a double density (720K)  3«"  disk  on  my 
        system: 

          flopskew b

          Find Optimal Head & Track Skew, Ver 1.0
          9 Sectors/Track, 80 Tracks, 2 Sides

          Head Skew Times (milliseconds):
          X:       0   1   2   3   4   5   6   7   8
          Time:   32  54  74  95 116 137 158 178 199

          Track Skew Times (milliseconds):
          Y:       0   1   2   3   4   5   6   7   8
          Time:  232  53  74  95 116 137 158 178 199

          Interleave:  1
          Minimum skewing parameters:  X=0, Y=1
          Recommended skewing parameters:  X=1, Y=2

        First  you are shown the format of the test diskette,  then  some 
        test results and finally the recommended skewing parameters.   If 
        you  are interested in some technical details about the test  you 
        should read the next few paragraphs; otherwise you can skip ahead 
        to  the  next section.   Just use the recommended  parameters  to 
        format  your disks and expect your diskette throughput to  become 
        about 30% faster. 

        Two  tests  are  run to find the best values for  the  Head  Skew 
        parameter  (X)  and the Track Skew parameter (Y).  The head  skew 
        test  is run by reading the last sector of the first track  using 
        head 0 and then measuring how long,  in milliseconds, it takes to 
        read  the first sector of that same track with head 1.   (If  the 
        disk is formatted with only one side this test is not run.)   The 
        track  skew  test is run by reading the last sector of the  first 
        track  using  head 1 (if testing a double sided disk)   and  then 
        measuring  how  long  it takes to read the first  sector  of  the 
        second track using head 0.  In the results above, the second line 
        tells  how  long this took,  in milliseconds,  for  each  of  the 
        sectors on the second track read. 
        
        Let's look at the example data to see what we can learn.   First, 
        notice  that the times to read different sectors in the head skew 
        test increase by about 22 milliseconds.  This is just the time it 
        takes to read one sector for this format.  The formula is 

          sector read time(ms) = 1000 * 60sec/min * rpm / sectors 

        For  this  format the drive rotates at 300  rpm and there  are  9 
        sectors  so  the  time  to  read  a  sector  works  out  to  22.2 
        milliseconds.  This formula can be modified to figure the time to 
        read  an entire track by dropping the final division by  sectors.  
        In this case, it is 200 ms.  
        
        To  determine the best values for X and Y,  the program finds the 
        smallest  time  and the corresponding number of  sectors  skipped 
        from the line above.  The data show that for my system no sectors 
        should  be  skipped when changing heads so the optimal head  skew 
        parameter,  X, is 0.  Typical values are 0 or 1 for most systems.  
        Now  look at the results for the track skewing test;  the time to 
        change tracks without skipping any sectors is 232!   This is  the 
        time  it  takes to read a whole track plus the sector  plus  some 
        overhead.   In this case the 0 sector skew provided by DOS format 
        and  the  default values used by FDFORMAT and ATFMT yield  a  big 
        waste  of  time when reading or writing multiple tracks.   On  my 
        system the optimal track skew parameter, Y, is 1.  Typically,  it 
        ranges from 1 to 3 on the systems I have looked at. 

        Now  notice  that  the program recommends  values  for  the  skew 
        parameters which are 1 greater than the optimal values.   This is 
        because the penalty for choosing a skew value which is too  small 
        is severe:  you have to wait a whole revolution, in this case 200 
        ms,   when changing tracks.   On the other hand,  the penalty for 
        having a skew value which is one too big is only 22  ms.    Since 
        some  software  may introduce an additional delay  when  changing 
        tracks,   it  is a safe bet to be conservative when choosing  the 
        skew values.   If you regularly use floppies on two computers you 
        should  run FLOPSKEW on both of them and choose the higher of the 
        recommended skew parameters. 

        Take  the values of X and Y found by the above procedure and  use 
        them to format your floppies in the future.   To make this  easy, 
        you  can create a batch file,  4DOS or CED alias,  or FDFORMAT or 
        ATFMT  configuration file with those parameters in it.   Any time 
        you format a floppy or read or write a floppy formatted this  way 
        it will go faster.  

        How much faster?   Well,  assuming the most likely case that only 
        track  seek is a problem and that the sector skewing is only  off 
        by  1 or 2,  then on average the computer has to wait for a  full 
        disk revolution every second track it reads.   Eliminate the wait 
        and  you  can reduce the time spent reading and writing  by  1/3.  
        When  formatting  a  diskette,  skewing only affects  the  verify 
        operation so the time reduction is somewhat less, about 20%. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± FLOPRPM ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        If   you  are  having  trouble  reading  or  writing   diskettes, 
        especially with a large number of sectors per track,  the problem 
        may  lie with the speed at which the drive spins.   FLOPRPM  will 
        test  this condition for you.   Simply place a formatted disk  in 
        the  drive you want to test and run FLOPRPM with the drive letter 
        as the only argument.  The program will then test and display the 
        rotation rate continuously until you press a key.   Normally, all 
        PC floppy drives will run within  an RPM or two of 300 except for 
        5¬"  HD drives which run at 360.   If you are having problems and 
        the  speed  of your drive is off by more  than that or the  speed 
        varies  a  lot,   you may  be able  to get  better  operation  by 
        adjusting the speed  of your drive.   Unfortunately,  no  general 
        guidelines  can  be  given  about how to do that  because  drives 
        differ in their design. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± FLOPINFO ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        This program  simply  reads the formatting information of  a disk 
        and displays it.   With all of the different formats supported by 
        FDFORMAT  and  ATFMT it's nice to know what format  a  particular 
        disk  is.    Also,  since some of these formats require a TSR  to 
        read,   you might want to know if a particular floppy can be read 
        on  another  system  which  doesn't  have  a  copy  of  that  TSR 
        available.   Or,  perhaps you want to quickly find out whether  a 
        floppy is HD or DD. 
        
        FLOPINFO  takes  one parameter,  the drive letter.   Here  is  an 
        example command and response, this time for a 1.4M 3«" disk. 

  flopinfo b

  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
  º     Floppy Disk Information, Ver. 1.1 by luitje@m-net.arbornet.org      º
  ÌÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍ¹
  º Sides ³ Tracks ³ Sec/Track ³ Bytes/Sec ³ Res/Hid Sec ³ Root Dir ³ Media º
  ÇÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ¶
  º   2   ³   80   ³    18     ³    512    ³    1 / 0    ³   224    ³   F0  º
  ÌÍÍÍÍÍÍÍÏÍÍÍÍÑÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÏÍÑÍÍÍÍÍÍÍÍÍÍÍÏÑÍÍÍÍÍÍÑÍÍÏÍÍÍÍÍÍÍ¹
  º  OEM Name  ³  Volume Name  ³ Vol Ser Num ³  FAT Type  ³ FATs ³ Capacity º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ¶
  º "MSDOS5.0" ³ "NO NAME    " ³  04DA-F7FE  ³ "FAT12   " ³   2  ³  1457664 º
  ÈÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍ¼

        The  Volume  Name displayed is from the boot  sector;   there  is 
        another  one in the root directory which may be different.    The 
        Volume Name, Volume Serial Number and FAT Type are not present on 
        disks  formated  with  versions  of DOS prior  to  4.0   and  are 
        displayed as dots in that case.  The "Res/Hid Sec"  box shows two 
        numbers,  the number of reserved and hidden sectors.   "Root Dir" 
        shows the number of files allowed in the root directory.  "Media" 
        is the media descriptor byte. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± FLOPSCRB ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        If you've ever bought one of those inexpensive disk cleaning kits 
        you've  probably  noticed that the instructions which  come  with 
        them are kind of skimpy.   Something like:  "squirt some cleaning 
        fluid  on  the  cleaning disk and then operate the drive  for  10 
        seconds". But how do you "operate the drive"? 

        You  could  use the dir command but it will time out with a  read 
        error  after  a  few  seconds so  you  have  to  keep  re-issuing 
        commands.   Even worse,  the dir command only tries to read track 
        zero  so  you  are  only using a small portion  of  the  cleaning 
        surface.  Or you could use other programs which access the  disk, 
        like format, but they all have the same problems:  it's difficult 
        to  control how long the cleaning is done and which part  of  the 
        cleaning disk is used. 

        FLOPSCRB  takes care of these problems and in addition  may allow 
        the cleaning disk to be used longer because of the way it manages 
        the cleaning process.  FLOPSCRB cleans the drive in three stages.  
        The  first stage uses the outside third (which  has  the  largest 
        area)   of  the  cleaning disk.   This removes the worst  of  the 
        accumulated oxide.  The second stage moves to the middle third of 
        the  disk  where any remaining particles are moved.    The  third 
        stage moves to the inner third of the cleaning disk to finish the 
        job.   With this sequence the head becomes progressively  cleaner 
        instead  of  just  rubbing  dirt off on  the  cleaning  disk  one 
        revolution and then picking it up the next. 

        FLOPSCRB only needs to be told which drive to clean (only A and B 
        are  supported  at this time)  and how long to run  the  cleaning 
        action.    To clean drive a for 15  seconds (5  seconds for  each 
        stage) you'd use the following command: 

          flopscrb a 15

        NOTE:  The abrasiveness of the cleaning pads may vary from kit to 
        kit  so  always  follow  the  manufacturer's  instructions  about 
        cleaning time. It may be possible to damage the floppy drive head 
        by cleaning the drive excessively. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Acknowledgements ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Outside  of the cryptic documentation for the NEC æPD765A  floppy 
        disk  controller  chip there is not a whole  lot  of  information 
        available  about the nitty gritty of controlling floppies.    I'd 
        like  to thank two freeware authors who have  written  worthwhile 
        programs  and then published the source code for others to  learn 
        from.   Christoph  Hochst„tter's FDFORMAT provides  lots  of good 
        examples of code for using the BIOS INT 13 calls and creating the 
        basic  disk  structure (it also lets you learn  a  little  German 
        along the way).  The 2M package by Ciriaco de Celis provides some 
        utilities  which really push the envelope of putting the  maximum 
        amount  of  information  on a floppy disk.   I  needed  to  issue 
        commands directly to the floppy drive controller to make FLOPSCRB 
        work and I learned how to  do  this (and some Spanish) by reading 
        his source code.   Understanding these programs can be slow going 
        if  you  don't  understand German and Spanish but it  sure  beats 
        disassembling  your  BIOS!  Look for them in  the  msdos/diskutil 
        directory of your local SimTel mirror. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Distribution ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The programs and documentation in the Floppy Tool Kit package are 
        copyrighted  works  of William Luitje.   The author grants you  a 
        non-exclusive license to copy and distribute these  works as long 
        as they are distributed as a group with no additional files added 
        to  the  archive  (this includes BBS ads)  and the  programs  and 
        documentation are not modified in any way. 

        On a related note, I am distributing these programs for free.  If 
        you paid money for a floppy or CD-ROM with these programs on  it, 
        be  aware that I am not seeing a penny of it.   What you paid for 
        is the service of distribution.  I'm sure that you understand the 
        nature of transactions like that but I have heard from people who 
        "bought  one  of  my  programs"   and  expect  me  to  conduct  a 
        correspondence course on basic PC  techniques,  theory and repair 
        because  of  their  "purchase".   While I am always open  to  bug 
        reports and well  thought out questions (and postcards!),  please 
        read  the  documentation carefully and check with  local  experts 
        before you fire up your word processor. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Liability ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        This  software  is intended to be safe to use.    All  tests  and 
        information  programs are read only so no data on your test disks 
        should be altered. FLOPSCRB and SEEKBNCH could conceivably damage 
        a drive if used inappropriately but I abused  my  drives quite  a 
        bit while writing and  debugging  these  programs and haven't had 
        any  problems.    About the only other problem you might have  is 
        that if you set the floppy drive parameters  too fast you may get 
        read or write errors.  Never the less, in using this software you 
        assume all risk should anything go wrong.  I think that is pretty 
        unlikely, but, hey, sometimes it rains fish! 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Registration ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        While this software may be freely copied and used,  I  do request 
        that  you  register  it if you use it.   Just send  me  either  a 
        postcard or some e-mail telling me which programs you find useful 
        and  which version of the package you are using.   This  is  only 
        partially an ego massage for the author.   I enjoy writing useful 
        utilities and have several other pieces of freeware out  floating 
        around  the  net so I would like feedback about which of them are 
        worth expanding and supporting. 

        William Luitje
        2677 Wayside Drive
        Ann Arbor, MI 48103
        USA

        Internet:  luitje@m-net.arbornet.org

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± History ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Version 1.0 20 Jan 94
           First  release with FLOPPARM, FLOPTEST, FLOPSKEW,  FLOPRPM and 
             FLOPINFO
        Version 1.1 13 Mar 95
           Changes to FLOPPARM:  tweaked FAST parameters, changed 
             allowable ranges of parameters
           Changes to FLOPINFO:  added volume name, volume serial number, 
           FAT type, hidden sectors and media byte to output.  Reorganized 
             display for readability.
           Minor internal changes to the rest of the programs.
           Added TESTSTEP
           Added SEEKBNCH
           Added FLOPSCRB

        Copyright 1994-1995 by William Luitje