KSP FTP (tm)

                      A FTP Door for Bulletin Board Systems










                                   Version 2.0










                               Copyright (C) 1995
                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                        Menlo Park, California 94025-1802
                              BBS/FAX: 415-364-9847



                KSP FTP is a trademark of Key Software Products.
                 PCL4C is a trademark of MarshallSoft Computing.
                     WATTCP is a trademark of Erick Engelke.
                     Power C is a trademark of Mix Software.
                   Lantastic is a trademark of Artisoft, Inc.
                      Novell is a trademark of Novell Corp.
                   Banyan Vines is a trademark of Banyan Inc.
             DESQview is a trademark of Quarterdeck Office Systems.





        



                                TABLE OF CONTENTS



        CHAPTER 1 - INTRODUCTION        ...........................    1
           1.1  Compatibility with BBS Software     ...............    1
           1.2  Hardware Requirements       .......................    2
           1.3  Software Requirements       .......................    2
           1.4  Other KSP Software      ...........................    2
              1.4.1  KSP Telnet       .............................    3
              1.4.2  KSP SLIP       ...............................    3
              1.4.3  So Many CD's      ............................    3

        CHAPTER 2 - INSTALLATION        ...........................    4
           2.1  Packet Driver Shims for Novell    .................    4
           2.2  Packet Driver Shim for Novell w/Token-RingSNAP   ..    5
           2.3  Packet Driver Shims for Lantastic    ..............    5
              2.3.1  Changes to CONFIG.SYS      ...................    5
              2.3.2  Changes to PROTOCOL.INI      .................    6
           2.4  Packet Driver Shims for Banyan Vines   ............    7
           2.5  Other Things to Configure     .....................    7

        CHAPTER 3 - THE WATTCP CONFIGURATION FILE     .............    8
           3.1  Multiple Nodes and the "include" Directive   ......    9
           3.2  Using a BOOTP Server     ..........................    9
           3.3  Manual Configuration       ........................    9
              3.3.1  The PC's Host Name     .......................   10
              3.3.2  The PC's Domain Name     .....................   10
              3.3.3  The PC's IP Address     ......................   10
              3.3.4  The Name Server's IP Address    ..............   11
              3.3.5  The Router's IP Address     ..................   11
              3.3.6  The PC's Network Mask     ....................   11
           3.4  TCP/IP Parameters (optional)      .................   11
              3.4.1  DNS Search Mode      .........................   12
              3.4.2  Timeouts        ..............................   13
              3.4.3  Maximum Segment Size (MSS)     ...............   13
           3.5  FTP Operating Parameters      .....................   13
              3.5.1  Dynamic Parameters       .....................   14
              3.5.2  Session Time Limit      ......................   14
              3.5.3  Session Reserve Time      ....................   15
              3.5.4  Inactivity Limit       .......................   15
              3.5.5  Minimum Baud Rate      .......................   15
              3.5.6  Operating Hours       ........................   15
              3.5.7  User Session Logging      ....................   16
              3.5.8  Non-Standard Port/Fossil Break Detect     ....   16
              3.5.9  Adding External Protocols      ...............   16
              3.5.10  Controlling Disk Space Usage     ............   17
              3.5.11  Limiting User Download Bytes     ............   18
              3.5.12  Updating BBS Download Bytes     .............   18
              3.5.13  Silencing the BBS console bell    ...........   19
              3.5.14  Disabling the Local Screen     ..............   19




        



                                TABLE OF CONTENTS


        CHAPTER 4 - INSTALLING THE FTP DOOR COMMAND    ............   20
           4.1  Command Line Parameters      ......................   20
              4.1.1  The /MAXMINS Parameter      ..................   21
              4.1.2  The /CONFIG Parameter      ...................   21

        CHAPTER 5 - INSTALLING YOUR ACCESS KEY     ................   22

        CHAPTER 6 - SELECTING A SERIAL COMMUNICATION PROTOCOL    ..   23
           6.1  Internal Protocols       ..........................   23
              6.1.1  Internal Xmodem and Ymodem Protocols    ......   23
              6.1.2  Internal 1K-Xmodem/G and Ymodem/G Protocols      23
              6.1.3  Internal Zmodem Protocol      ................   24
           6.2  External Protocols       ..........................   24
           6.3  Recommendations        ............................   24

        APPENDIX 1 - HOW TO REACH US     ..........................   26

        APPENDIX 2 - GETTING UPDATES VIA THE INTERNET    ..........   27

        APPENDIX 3 - LEGAL STUFF       ............................   28
































        




        Aug 20, 1995            KSP FTP (tm) v2.0                       1


                        CHAPTER 1 - INTRODUCTION        


        KSP  FTP  is  a  BBS door that implements the familiar FTP client
        program  that  allows  users  to  transfer  files  to/from remote
        computers  over  a  TCP/IP  network.  If your BBS is connected to
        the  Internet,  KSP  FTP  lets your BBS callers transfer files to
        and  from remote host machines anywhere in the world for the cost
        of a phone call to your BBS! 

        During  file  transfers, data between the BBS and the remote host
        is  transmitted using the TCP/IP protocol, while data between the
        BBS  and  the  user  is  transmitted using a serial communication
        protocol  such  as X/Y/Zmodem.  Both internal and external serial
        communications   protocols   are  supported;  internal  protocols
        include  Xmodem-Cksm, Xmodem-CRC, 1K-Xmodem, 1K-Xmodem/G, Ymodem,
        Ymodem/G, and Zmodem.  

        KSP FTP meets the following BBS-specific needs: 

             1.  Terminates  the  BBS session when user's time limit
                     expires.  
             2.  Terminates the BBS session when user hangs up.  
             3.  Terminates   when   there's   no   activity  for  a
                     sysop-specified period of time.  
             4.  Records the FTP session in a log file.  
             5.  Provide  colorized  or  parameterized  messages  to
                     user.  
             6.  Restrict users by baud rate.  
             7.  Restrict hours of operation.  

        KSP   FTP   is   shareware.   The  unlicensed  version  is  fully
        functional  except  that it imposes a maximum of five minutes per
        FTP  session.   Once  licensed,  the  user is limited only by the
        amount of time remaining in his BBS session.  

        KSP  FTP  was  implemented  using  Erick  Engelke's  Waterloo TCP
        library,  MarshallSoft  Computing's PCL4C Personal Communications
        library  and  PPL4C Personal Protocol Library, and Mix Software's
        Power C compiler.  


        1.1 Compatibility with BBS Software      

        KSP  FTP  is compatible with any BBS software that can generate a
        DOOR.SYS  file.   It  works  with  a  BBS  configured  to use the
        standard  COM1  through  COM4 ports, or will automatically detect
        and use a Fossil driver.  




         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       2



        1.2 Hardware Requirements        

        KSP  FTP  inherently  requires  that  the  PC  running  your  BBS
        software  have  a  physical  connection  to  a  TCP/IP  network -
        normally  the  Internet.  Ideally, this connection is by means of
        an  adapter  card  connected  to  an  Ethernet at your company or
        school (and then through a "gateway" to the Internet).  

        It  is  also  possible  to  connect  to  the  Internet  through a
        commercial  Internet  Access  Provier  via  a dial-up FTP (Serial
        Line  Internet  Protocol)  connection.   This approach requires a
        second  serial  port, modem, and telephone line dedicated to this
        purpose.   Information on finding such a provider is available on
        the KSP BBS.  


        1.3 Software Requirements        

        KSP  FTP  runs  on  top  of  another  piece  of software called a
        "packet  driver".  The packet driver presents a standard software
        interface  to  KSP  FTP,  regardless  of  the  type  of  hardware
        interface  that  connects  the  PC to the network.  Public domain
        packet  drivers  exist  for  SLIP and PPP links and most Ethernet
        cards.  

        If  your  BBS  uses  a  multi-tasking  operating  system  to  run
        multiple  nodes  on  a  single  PC,  then you will need a "packet
        multiplexer".   A  packet  multiplexer  designed specifically for
        use   with   KSP  network  products  running  under  DESQview  is
        available  as  a  freeware  package  distributed  as KSPMUX*.ZIP,
        where  the  "*"  is  the  version  number.   KSP  FTP is DESQview
        "aware"   to   provide   better  performance  in  a  multitasking
        environment.  

        If  your  PC  is  connected  to  a non-TCP/IP proprietary network
        (such  as  Novell  or Lantastic), you will probably need a packet
        driver "shim".  

        KSP  FTP  does  NOT  require  that you purchase a separate TCP/IP
        package,  such as that sold by Novell, Artisoft, or IBM.  KSP FTP
        should happily coexist with any of these packages, however.  

        An  assortment of public domain packet drivers, multiplexers, and
        shims are available on the KSP BBS.  







         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       3


        1.4 Other KSP Software       

        Key  Software  Products  offers  a  number  of other products for
        BBS's: 


        1.4.1 KSP Telnet        

        A   door  program  that  allows  callers  to  connect  to  remote
        computers  anywhere  on the Internet via your BBS.  Available now
        on our BBS.  


        1.4.2 KSP SLIP        

        A  door  program  that  allows callers to run any TCP/IP software
        from  home,  including using Mosaic to browse the World Wide Web.
        Available now on our BBS.  


        1.4.3 So Many CD's       

        A  PCBoard PPE to handle off-line CD-Roms.  Seamlessly integrated
        into  PCBoard.   Users  post requests for off-line files and have
        then  returned  as  attachments to messages. Configurable message
        pack-out  dates  automatically  keep  your hard disk from getting
        cluttered.  Available now on our BBS.  

























         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       4


                        CHAPTER 2 - INSTALLATION        


        Before installing KSP FTP as a BBS door, you must first install: 

             1.  The network interface hardware.  
             2.  A corresponding packet driver.  
             3.  A packet driver shim (if needed).  
             4.  A packet multiplexer (if needed).  

        Detailed  directions for these preliminary steps are available in
        separate   documentation   that   comes  with  the  corresponding
        hardware or software.   

        It's  most  common  that multi-node BBS's are interconnected with
        Ethernet  and  either  Lantastic or Novell.  Unfortunately, these
        two  network  operating  systems  were  designed  using their own
        proprietary  protocols  rather than the TCP/IP protocol and their
        own  proprietary  software  rather than packet drivers to talk to
        their  Ethernet  interface  cards.   However, a piece of software
        called  a packet driver "shim" can be used to let both TCP/IP and
        their proprietary protocol coexist.  


        2.1 Packet Driver Shims for Novell     

        Novell's  network  software is installed in layers as TSRs in the
        order  shown  below.   These commands are usually found either in
        the  AUTOEXEC.BAT  file  or  in another batch file in a directory
        typically called C:\NWCLIENT.  

             LSL
             NE2000  }-- specific to your interface card
             IPXODI
             VLM

        The  packet driver shim (ODIPKT) logically sits on top of IPXODI,
        providing  a  packet  driver  interface  for software such as KSP
        FTP: 

             LSL
             NE2000 +--- Frame Type (0-3)
             IPXODI |
             ODIPKT 2 97  }--- The packet driver shim
             VLM       |
                       +----- Packet Vector Interrupt (96-127)
                              (See comment below about hex vs. decimal)

        The  ODIPKT  command  line parameters may vary according to which



         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       5


        version  of  the  software  you  have  and  how  your hardware is
        configured.   The "Frame Type" parameter should correspond to the
        position  of  ETHERNET_II  among  the  frame  types  specified in
        NET.CFG;  zero  (0)  selects  the  first  frame type, one (1) the
        second,  and  so on.  The "Packet Vector Interrupt" number should
        correspond  to  an  unused  interrupt  vector.   Note  that older
        versions  of  ODIPKT  insist that this number be given in decimal
        (96-127)  rather  than  in hex (0x60-0x7F).  The necessary packet
        driver  shim can be downloaded from the Key Software Products BBS
        as file ODI-SHIM.ZIP.   


        2.2 Packet Driver Shim for Novell w/Token-RingSNAP    

        Another  shim  called  ODITRPKT  exists for Novell that should be
        used  if the underlying network is Token-Ring_SNAP.  Installation
        is  similar  to  ODIPKT as described above, except that the first
        command  line  parameter  must  correspond to the Token-Ring_SNAP
        frame  type  in NET.CFG, and starts at "1" rather than "0".  This
        shim  can  be  downloaded  from  the Key Software Products BBS as
        file TKN-SHIM.ZIP.  


        2.3 Packet Driver Shims for Lantastic     

        Using   a   packet  driver  shim  with  Lantastic  requires  that
        Lantastic  be  installed  using  NDIS  (Network  Driver Interface
        Specification)  Support.  The necessary packet driver shim can be
        downloaded   from   the   Key   Software  Products  BBS  as  file
        DIS-SHIM.ZIP.  

        NDIS   allows  you  to  stack  multiple  protocols  on  a  single
        adapter.   This  lets  you use multiple protocol drivers (such as
        LANtastic  and  TCP/IP)  on  the  same adapter.  You can also use
        NDIS  to  include  third-party adapters that have NDIS drivers in
        your   LANtastic   network.    Supported  adapter  types  include
        Ethernet,  Token-Ring  and ARCNET (R) adapters.  The software and
        documentation  necessary  to  add  NDIS  support  to  an existing
        Lantastic network is available free of charge from Artisoft.  

        Once  you  have NDIS installed and working with Lantastic, adding
        the  shim is a simple matter of editing PROTOCOL.INI (part of the
        NDIS support) and CONFIG.SYS.  









         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       6


        2.3.1 Changes to CONFIG.SYS       

        With  NDIS  installed,  there  will be two device driver lines in
        your CONFIG.SYS file that look something like the following: 

             DEVICE=C:\LANTASTI\PROTMAN.DOS /I:C:\LANTASTI
             DEVICE=C:\LANTASTI\AEXNDIS.DOS

        The  file  listed  in  the  second line may differ if you are not
        using  Artisoft's  interface  card; in that case, this file would
        typically  be  replaced  by  a  NDIS  driver supplied by the card
        manufacturer.  

        The  packet  driver  shim  itself  is installed as a third device
        driver after the first two, as in: 

             DEVICE=C:\LANTASTI\PROTMAN.DOS /I:C:\LANTASTI
             DEVICE=C:\LANTASTI\AEXNDIS.DOS
             DEVICE=C:\DRIVERS\DIS_PKT.DOS  }--- The packet driver shim


        2.3.2 Changes to PROTOCOL.INI       

        The  PROTOCOL.INI  file  is  a  text file created (usually in the
        C:\LANTASTI  directory) as part of the NDIS installation.  Before
        adding  the  packet  driver  shim,  it  typically  looks like the
        following,  but  with  the  "iobase"  and  "interrupt" parameters
        changed   according   to   your  hardware,  or  with  the  entire
        "[AEXNDIS_NIF]"   section  replaced  if  you  are  not  using  an
        Artisoft interface card.  

             [PROTMAN]
               DRIVERNAME = PROTMAN$
               DYNAMIC = YES

             [AEXNDIS_NIF]
               DRIVERNAME = AEXNDS$
               IOBASE = 0x300
               INTERRUPT = 15

        Adding  the packet driver shim requires adding another section to
        the PROTOCOL.INI file: 

             [PROTMAN]
               DRIVERNAME = PROTMAN$
               DYNAMIC = YES






         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       7


             [AEXNDIS_NIF]               <---+
               DRIVERNAME = AEXNDS$          |
               IOBASE = 0x300                |
               INTERRUPT = 15                | These names must match!
                                             |
             [PKTDRV]                        |
               DRIVERNAME = PKTDRV$          |
               BINDINGS = AEXNDIS_NIF    <---+
               INTVEC = 0x61
               CHAINVEC = 0x66
               NOVELL = Y

        Note  that the name "AEXNDIS_NIF" must exactly match the spelling
        used  as  the  title of the previous section, "[AEXNDIS_NIF]"; if
        you  are not using Artisoft interface cards, then both occurences
        will  use  some  other identifier.  The "INTVEC" parameter may be
        anything  from  0x60  to 0x80; you may have to experiment to find
        an unused interrupt number.  


        2.4 Packet Driver Shims for Banyan Vines    

        Although  Key  Software  Products  has  never  used  it, and thus
        cannot  offer help on its installation, a packet driver shim does
        exist  for  Banyan  Vines  and  can  be  downloaded  from the Key
        Software Products BBS as file BAN-SHIM.ZIP.  


        2.5 Other Things to Configure      

        Once  your  network  is  up and running with a packet driver or a
        packet driver shim, there are basically two additional steps: 

             1.  Create a WATTCP.CFG configuration file.  
             2.  Configure KSP FTP as a BBS door.  

        As  discussed  in the next chapter, you may not need a WATTCP.CFG
        configuration file if you have a BOOTP server.  

        There  is  a  useful  program called TCPINFO available on the KSP
        BBS.   If  you have no WATTCP.CFG file, it will tell you (after a
        maximum  of 30 seconds) if it was able to automatically configure
        itself  via  a  BOOTP  server.  If you have a WATTCP.CFG file, it
        will  determine  whether  or  not  you  have configured that file
        properly.  







         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       8


                 CHAPTER 3 - THE WATTCP CONFIGURATION FILE     


        In  order  to  run,  KSP FTP needs to know some information about
        your  network,  and  tries  to  find this in a configuration file
        called  WATTCP.CFG.  KSP FTP looks in three directories to locate
        this  file.   First, it checks for an environment variable called
        WATTCP.CFG  that  specifies  the  directory.  Second, it looks in
        the  current  (default) directory.  Third, if still not found, it
        looks   in   the   directory   that   contains   the   executable
        (KSP-FTP.EXE).   

        The  following  example  may  be  helpful  for  those  using  the
        environment  variable  approach:  If you place WATTCP.CFG in your
        PCB  directory,  then  your  AUTOEXEC.BAT file should contain the
        following command: 

                              set WATTCP.CFG=C:\PCB

          Note that there is no trailing "\" after the directory name!

        If  KSP  FTP  still  can't  find  the configuration file, it will
        attempt  to  automatically  configure  itself  by  looking  for a
        "BOOTP"  server  on  your network.  (BOOTP is a standard protocol
        that  obtains  your "IP address" and other information about your
        PC  from  a  BOOTP  server.)   If there is no BOOTP server, or if
        your  PC  is not registered in its database, then you must create
        a configuration file.  

        The  configuration  file  contains  one entry per line.  A sample
        configuration  file  is  included  in  this distribution, but the
        values  MUST  be  modified to suit your particular environment or
        else KSP FTP will not work!   

        The syntax of every entry follows the following format: 

           [ directive = [ "data" | data] ] [ # comment | ; comment ]

        I.e.,  if  a  directive is not followed by data, the directive is
        ignored.   Similary,  lines  without directives are ignored.  The
        directive is NOT case sensitive; the data IS case sensitive.   

        e.g.,   netmask=255.255.252.0
                domainslist=ksp.com    ; Our domain

        Whitespace  is normally removed from data; data containing blanks
        must  be  surrounded by quotes.  An unquoted '#' or ';' marks the
        beginning of a comment.  




         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                       9



        3.1 Multiple Nodes and the "include" Directive    

        There  must  be  one WATTCP.CFG file for each BBS node since each
        node  has  to  be  configured  with  a  unique  hostname  and  IP
        address.   All  other configuration parameters are usually set at
        the  same  values  for  all nodes.  Rather than duplicating these
        common  entries  in each WATTCP.CFG file, you can set-up a master
        configuration   file   that   gets  "included"  in  each  of  the
        node-specific   files.    For  example,  the  node-specific  file
        (WATTCP.CFG) might look like: 

                include=c:\ksp\master.cfg
                hostname=ourbbspc
                myip=125.283.210.17

        This  makes it much easier to make changes since you only have to
        modify a single file (MASTER.CFG).  


        3.2 Using a BOOTP Server      

        It's  always  a good idea to have a configuration file whether or
        not   you   use   a  BOOTP  server.   If  you  choose  to  use  a
        configuration  file  and want to tell it to use the BOOTP server,
        this  option  allows  you  to specify your the IP address of your
        BOOTP server.  


                Example: bootp=129.255.0.128 

        You  should  specify the domain name manually as described in the
        next  section  since  the  BOOTP  protocol  doesn't  provide that
        information.  

                Example: domainslist=ksp.com 

        NOTE:  An  "IP  address"  is  a logical addressing scheme used on
        TCP/IP  networks  such  as the Internet.  Each computer connected
        to  the  Internet  is  assigned  a unique IP address.  Your local
        network  "guru"  or access provider should be able to provide you
        with those IP addresses you need.   

        IMPORTANT:  The  IP  addresses  given  in  this document are only
        examples.   Do  NOT  attempt to use them - they will NOT work and
        your network administrator will probably get VERY upset! 






         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      10


        3.3 Manual Configuration        

        If  you  don't  have  a  BOOTP  server,  or  if  your  PC  is not
        registered  with  a BOOTP server, then you must use the following
        directives  to configure KSP FTP.  The values of these parameters
        are  important,  and  KSP  FTP will NOT function properly without
        the   proper   values.    If   you  are  not  familiar  with  the
        terminology,  or  if  you are unsure of the proper values, please
        consult with your network access provider.  


        3.3.1 The PC's Host Name      

        This  is  the network name of the PC that runs your BBS (and thus
        KSP  FTP).  If your BBS is implemented by a network of PC's, then
        each PC should have its own unique host name.  

                Example: hostname=bbs 

        Note  that  the  host  name  does  not  include  the  domain name
        suffix.   For  example, the hostname of machine '"bbs.ksp.com" is
        simply "bbs".  


        3.3.2 The PC's Domain Name      

        This  is  the  network  name  of the subnet to which your PC (and
        possibly others) are connected.  

                Example: domainslist=ksp.com 

        Note  that  the  domain  name  does  not  include  the  host name
        prefix.   For  example, the domain name of machine '"bbs.ksp.com"
        is "ksp.com".  


        3.3.3 The PC's IP Address      

        This is the unique IP address assigned to your PC.  

                Example: my_ip=100.2.37.4  

        Your  local  network  "guru" or access provider should be able to
        provide  you  with  the  proper IP address of your PC.  Note that
        you  should  have  a  different  IP address for each node in your
        BBS.  

        Note:  As  an  alternative, you may also set the IP address using
        an environment variable, as in: 



         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      11



                              set ksp-ip=100.2.37.4


        3.3.4 The Name Server's IP Address     

        This  is  the  unique  IP  address  assigned  to  a  network name
        nerver.   You  may  specify more than on nameserver by using more
        than one "nameserver" line.  

                Example: nameserver=111.21.108.110 

        Your  local  network  "guru" or access provider should be able to
        provide  you  with the proper IP addresses of appropriate network
        name servers.  


        3.3.5 The Router's IP Address      

        This is the unique IP address assigned to the network router.  

          Syntax: gateway = ipaddr [ , subnet [ , subnet_mask ] ] 

                Examples: gateway=129.97.176.1
                          gateway=129.97.176.2, 129.97.0.0
                          gateway=129.97.176.2, 129.97.0.0, 255.255.0.0

        Usually  the  (destination)  subnet  and  subnet mask need not be
        specified,  and  is  used to create a "default".  The other forms
        are  used  to  specify  one or more other gatewaya for particular
        subnets.  

        Your  local  network  "guru" or access provider should be able to
        provide you with the proper IP address of the network router.  


        3.3.6 The PC's Network Mask      

        Network  masks  are  used to distinguish destination IP addresses
        that  are  on  the  local  subnet  from those that are not.  This
        option may not be required, depending on your network topology.  

                Example: netmask=255.255.254.0 

        Your  local  network  "guru" or access provider should be able to
        provide you with the proper netmask if needed.  






         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      12


        3.4 TCP/IP Parameters (optional)       

        KSP  FTP  will  work  without using the following parameters, but
        they are provided if you wish to change them.  


        3.4.1 DNS Search Mode       

        A  remote  hostname  (e.g.,  ralph.ksp.com) is translated into an
        numeric  IP  addresse  (e.g.,  128.16.202.12)  by  a  nameserver.
        Sometimes,  however,  users  enter  hostnames  in  an abbreviated
        form.   For  example,  if  the local machine (e.g., ruby.ksp.com)
        was   in   the   same   domain   (ksp.com)  as  the  remote  host
        (ralph.ksp.com),  then  perhaps  only the remote hostname (ralph)
        might  be given.  Short versions like this must be fully expanded
        (e.g.,  ralph.ksp.com)  before  a  nameserver  can translate them
        into an IP address.  

        Waterloo  TCP/IP  solves  this  by  feeding the nameserver with a
        sequence  of  constructions  formed  from the remote hostname and
        the  local machine's domainslist.  For a remote hostname given as
        "a.b"  and  a  domainslist  specified  in  WATTCP.CFG  as  "c.d",
        Waterloo  TCP/IP  would  attempt  name  server  lookups  first on
        "a.b.c.d",  then  on  "a.b.d",  and then on "a.b".  Although this
        approach  is  guaranteed to find the appropriate construction, it
        can  waste  time  performing  nameserver  lookups  on  improbable
        constructions.  

        Consider  the sequence of constructions attempted when the remote
        hostname   is  "garbo.uwasa.fi"  and  the  local  domainslist  is
        "ksp.com": 

                (1) garbo.uwasa.fi.ksp.com      -> fails
                (2) garbo.uwasa.fi.com          -> fails
                (3) garbo.uwasa.fi              -> succeeds

        We've  modified  Waterloo  TCP/IP's search strategy to accelerate
        name  server  lookups  by  adding three optional mode variations,
        enabled   by   specifying   one   of   the  following  WATTCP.CFG
        configuration parameters: 

        dns_search_mode=map_local_names 

            Abbreviated  (local)  hostnames  that do not contain a period
            are   processed  in  the  normal  (Waterloo  TCP/IP)  manner.
            Otherwise,  hostnames  like  "garbo.uwasa.fi"  are  attempted
            immediately  without  modification.   This is the recommended
            search mode.  




         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      13


        dns_search_mode=fully_specified 

            This  mode  passes  the  hostname  directly to the nameserver
            without  modification.   I.e.,  it assumes that hostnames are
            always  fully  specified  by  the  user without abbreviation.
            Abbreviated   names  will  not  be  translated  and  will  be
            returned by the nameserver as unknown.  

        dns_search_mode=recognized_root 

            Remote  hostnames  ending in the common domain suffixes (com,
            edu,   gov,   mil,   net,  org,  nato,  arpa)  are  attempted
            immediately  without  modification.   All other hostnames are
            processed  in  the normal manner.  (Note that this mode is no
            better  than  the  normal Waterloo TCP/IP strategy with names
            like "garbo.uwasa.fi".) 


        3.4.2 Timeouts         

        Most  network  operations (such as establishing a connection to a
        remote  host)  have a maximum time before a timeout error occurs.
        The  default  value is 30 seconds; a smaller value is unwise, but
        larger   values   may   be   necessary   for   particularly   bad
        connections.  

                Example: sockdelay=40 


        3.4.3 Maximum Segment Size (MSS)      

        The  default  value  of  MSS  is  1400.  If you know what maximum
        segment  size  means  and know what size you want, you can change
        it: 

                Example: mss=512 

                Note: Some  Internet  access  providers  configure  their
        dial-up  slip  and  ppp  accounts with a very small segment size.
        You  may  need  to  set  mss  as  low  as  212  if  your Internet
        connection is through such a connection.  


        3.5 FTP Operating Parameters       

        The  remaining  parameters in WATTCP.CFG are operating parameters
        for  KSP  FTP  that  define limits and display files needed while
        KSP FTP is running.  Each follows the format: 




         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      14


                ksp-ftp.<parameter>=<value> 

        where   <parameter>  and  <value>  are  replaced  by  appropriate
        strings.  

        Some  operating  parameters have counterparts in other members of
        the  KSP  family  of  network  application programs.  Rather than
        have   multiple   entries   in   the  WATTCP.CFG  file  for  each
        application,  such parameters can be specified globally using the
        format: 

                ksp.<parameter>=<value> 

        This  global setting can be overridden for a specific application
        by  using  the  application-specific form at a subsequent line in
        WATTCP.CFG.  


        3.5.1 Dynamic Parameters        

        Configuration  file  parameters  can  be  made  "dynamic".   Such
        parameters  are ignored unless activated by an associated command
        line option: 

                /CONFIG=<number> 

        where  "<number>"  is  a non-zero integer.  Dynamic configuration
        parameters  are  those that specify a number in square backets as
        in: 

                ksp-ftp[<number>].<parameter>=<value> 

        The  number  specified  in the configuration parameter must match
        that  in  the  command  line  option  or  else  the configuration
        parameter will be ignored.  

        This also works for dynamic global parameters of the form: 

                ksp[<number>].<parameter>=<value> 













         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      15


        3.5.2 Session Time Limit       

         Syntax: ksp-ftp.max_mins=<number> 

        Example: ksp-ftp.max_mins=30 

        Purpose: Overrides  the  time  remaining as specified in DOOR.SYS
                 if  lower.  If omitted, time remaining is that specified
                 by DOOR.SYS.  


        3.5.3 Session Reserve Time       

         Syntax: ksp-ftp.reserve_mins=<number> 

        Example: ksp-ftp.reserve_mins=3 

        Purpose: Reduces  the  time available in the door so that if time
                 runs  out,  the  user  still  has a small amount of time
                 left  on  the BBS.  This is useful, for example, if your
                 BBS  offers  a  Time  Bank  so  that users can use it to
                 withdraw extra time.  


        3.5.4 Inactivity Limit        

         Syntax: ksp-ftp.idle_mins=<minutes> 

        Example: ksp-ftp.idle_mins=10 

        Purpose: Establishes  an  upper limit on how long the session can
                 remain  inactive  before  it is terminated.  If omitted,
                 no inactivity limit is imposed.  


        3.5.5 Minimum Baud Rate       

         Syntax: ksp-ftp.minbaud=<baudrate>[,<security>] 

        Example: ksp-ftp.minbaud=9600 

        Example: ksp-ftp.minbaud=9600,100 

        Purpose: Specifies  a  minimum  baud  rate  required  to  use the
                 gateway,  and  an  optional  security  level required to
                 override  the minimum baud rate.  If omitted, no minimum
                 baud rate will be required.  





         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      16


        3.5.6 Operating Hours        

         Syntax: ksp-ftp.ophours=<hh:mm-hh:mm> 

        Example: ksp-ftp.ophours=21:00-23:00 

        Purpose: To  establish  the  hours  of operation for the gateway;
                 attempts  to  use  the  gateway  at  other times will be
                 disallowed.    Times   must  be  specified  in  24  hour
                 format.   If  omitted,  the  gateway  may be used at any
                 time.  


        3.5.7 User Session Logging       

         Syntax: ksp-ftp.log_dir=<pathspec> 

        Example: ksp-ftp.log_dir=c:\ksp-ftp 

        Purpose: Specifies  the  name  of a directory where a log of user
                 sessions   will  be  kept.   The  log  files  are  named
                 KSP-FTP.???, where "???" is the BBS node number.  


        3.5.8 Non-Standard Port/Fossil Break Detect      

         Syntax: ksp-ftp.serial_port=<adr>,<irq> 

        Example: ksp-ftp.serial_port=3F8,5 

        Purpose: Used  to  override serial port and IRQ values implied by
                 "COMx"    in    DOOR.SYS    to    support   non-standard
                 configurations  that  are  NOT  using  a  fossil driver.
                 Also  used  WITH  a  fossil  driver  to add serial break
                 detection.  

                 The  port  address  <adr>  must be specified in hex, and
                 the   interrupt   request  line  number  <irq>  must  be
                 specified in decimal.  


        3.5.9 Adding External Protocols       

         Syntax: ksp-ftp.protocol=<letter>,<T|F>,<title> 

        Example: ksp-ftp.protocol=S,T,SEALink 


                 Purpose:  KSP  FTP  provides  internal  support  for the



         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      17


                 Xmodem-Cksm,    Xmodem-CRC,    1K-Xmodem,   1K-Xmodem/G,
                 Ymodem,   Ymodem/G,   and  Zmodem  protocols.   However,
                 additional  "external" protocols can be added using this
                 option.    (Be   sure   to  read  the  chapter:  "SERIAL
                 COMMUNICATION PROTOCOLS").  

                 Each  external  protocol requires that you specify three
                 parameters: 

                    <letter>        The letter used to select the protocol.

                 <T|F>           "T" if the protocol supports batch transfers.

                 <title>         A short identifying phrase.

                 NOTE:   The  following  letters  are  used  to  identify
                 internal  protocols.   If  one  of these letters is used
                 with  this  option,  the  external protocol will replace
                 the corresponding internal protocol.  

                    X       Xmodem-Cksm
                 C       Xmodem-CRC
                 O       1K-Xmodem
                 F       1K-Xmodem/G (download only)
                 Y       Ymodem
                 G       Ymodem/G    (download only)
                 Z       Zmodem

                 Internal  protocols  do  not require the use of BBS disk
                 space.   KSP FTP simply reformats the data blocks during
                 a  transfer:  data  transmitted  between the BBS and the
                 remote  host use FTP's TCP/IP protocol; data transmitted
                 between  the  BBS  and  the  user  use  a modem-to-modem
                 protocol.  

                 External  protocols  are  implemented  by other programs
                 that   KSP  FTP  loads  and  executes.   These  programs
                 implement  only  a  modem-to-modem protocol and designed
                 to  transfer  a  file from the disk out over a telephone
                 line  or  vice-versa.  Therefore, when using an external
                 protocol  to  transfer  a file from a remote host to the
                 user,  KSP  FTP first transfers the entire file from the
                 remote  host  to  the  BBS  disk  using TCP/IP, and then
                 executes  the  external  protocol  to  transmit the disk
                 file  to  the  user.   Uploads to a remote host using an
                 external protocol do the same but in reverse.  






         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      18


        3.5.10 Controlling Disk Space Usage      

         Syntax: ksp-ftp.mb_external=<megabytes> 

        Example: ksp-ftp.mb_external=10 


                 Purpose:  To  limit  the  amount  of  BBS temporary disk
                 space used by external protocols for file transfers.  

                 When  a  user  downloads a file from a remote host using
                 an  external  protocol,  the  entire  file must first be
                 transferred  to  a  temporary directory on the BBS disk.
                 Since  filenames  can  be requested using wildcards, and
                 since  TCP/IP  transfer  rates  approach 1 MB/Sec, it is
                 quite  possible  that  one request could quickly consume
                 all  of  the  BBS disk space.  This option prevents that
                 from happening! 

                 If  this  option  is  specified, the user is informed at
                 the  beginning  of a external protocol transfer how much
                 disk  space  may  be  used  for the temporary storage of
                 transferred  files.   KSP FTP will then monitor how much
                 disk  space  is actually used and abort the remainder of
                 the request if the limit is exceeded.  


        3.5.11 Limiting User Download Bytes      

         Syntax: ksp-ftp.kb_limit=BBS | <kilobytes> 

        Example: ksp-ftp.kb_limit=BBS Example: ksp-ftp.kb_limit=2048 

        Purpose: Limit   the   number   of  kilobytes  that  a  user  may
                 download.   If set to "BBS" as in the first example show
                 above,  the  limit  is  that imposed by the user's quota
                 controlled  by  the  BBS.   If set to a number as in the
                 second  example,  the  number  will  be  the  number  of
                 kilobytes  per  FTP  session  -  regardless  of how many
                 times  the  user  enters  the  KSP FTP door while logged
                 into the BBS.  


        3.5.12 Updating BBS Download Bytes      

         Syntax: ksp-ftp.download_report=<filespec> 

        Example: ksp-ftp.download_report=c:\ksp\download.dat 




         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      19


        Purpose: Records  the  number  of bytes downloaded during the FTP
                 session  in  a file whose name (optionally preceded by a
                 drive  and directory prefix) is given in the option.  If
                 the  file  already  exists, it will be erased before the
                 new  information is recorded.  The format of the file is
                 extremely  simple:  one  line  of  text  containing  the
                 decimal number of bytes that were downloaded.  

                 The  data recorded in the file can be used to update the
                 user's   download   allocation.    However,  since  each
                 manufacturer's  BBS software is different from the next,
                 it  is  the  sysop's  responsibility  to  write  a small
                 program  that  will  take  the  content of this file and
                 modify the BBS's database.  


        3.5.13 Silencing the BBS console bell     

         Syntax: ksp-ftp.local_bell=<option> 

        Example: ksp-ftp.local_bell=disabled 

        Purpose: Used to silence the bell on the local BBS console.  


        3.5.14 Disabling the Local Screen      

         Syntax: ksp-ftp.local_screen=<option> 

        Example: ksp-ftp.local_screen=disabled 

        Purpose: Improves  caller's  display  speed  by  displaying  only
                 prompts   and   user   response  on  local  BBS  screen.
                 Eliminates   local   display   of   directory   or  file
                 contents.  

                 Note:  Pressing Shift-F1 on the local console of the BBS
                 while   a  caller  is  in  the  door  will  toggle  this
                 setting.  













         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      20


                 CHAPTER 4 - INSTALLING THE FTP DOOR COMMAND    


        Install  KSP  FTP  as  you  would  any other door program on your
        BBS.   Be  sure  you  setup the BBS to create a DOOR.SYS file for
        KSP  FTP  when it runs.  (KSP FTP does not need a USER.SYS file.)
        If  you are running multiple BBS nodes accessing a single copy of
        the  file  KSP-FTP.EXE,  then  don't  forget  to  make  that file
        read-only  using the DOS ATTRIB command in order to avoid sharing
        conflicts.  

        Most  BBS's  use  a  batch  file  to run a door.  For example, on
        PCBoard  systems  you might create a door batch file called "FTP"
        containing simply: 

                C:\FTP\KSP-FTP 
                BOARD 

        Do  NOT  change  directories  within  this  batch  file!  KSP FTP
        expects  to  find  the  DOOR.SYS  file in whatever is the default
        directory  at  the  moment it starts to run.  That's why the name
        of  the  program  is preceeded by the name of the directory where
        it is located.  

        Of  course, you must also configure your BBS so it knows where to
        find this batch file (FTP).  


        4.1 Command Line Parameters       

        In   PCBoard,  "%PCBDOOR%"  is  replaced  by  the  value  of  the
        environment  variable  called  "PCBDOOR"  which  is  set  to  the
        command  line  parameters  (if any) entered with the door command
        before  exiting  to  run  the  door.   For  example,  the PCBoard
        command: 

                FTP scuacc.scu.edu 

        sets  the  environment  variable  "PCBDOOR"  to  "scuacc.scu.edu"
        before  exiting  to  run  the  door.  Effectively, the batch file
        "FTP" becomes: 

                KSP-FTP scuacc.scu.edu 
                BOARD 

        If  a  host  name or IP address is given (as above), KSP FTP will
        automatically  connect  to  that host at startup, and will return
        to  the  BBS  as  soon  as the session with that host is finished
        (e.g., the user logs out).  



         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      21



        If  no  command  line parameter is given, KSP FTP will prompt the
        user  for  the host name when the door starts to run.  Unlike the
        situation  described  above,  when  the user logs out of a remote
        host,  control  is  returned  to KSP FTP command mode so that the
        user can then connect to a different host.  

        A  second  (third)  command  line  parameter  may  be provided to
        specify  the  login  name (password).  I.e., the complete command
        line syntax is: 

            KSP-FTP [<name_or_IP> [<login_name> [login_password]]] 

        where the square brackets "[]" indicate optional parameters.  

        There  are  two  additional  command  line parameters that may be
        used: 


        4.1.1 The /MAXMINS Parameter       

        The  /MAXMINS  parameter  is an alternative to the same parameter
        that  appears  in  the  WATTCP.CFG  file.   It  provides  another
        mechanism  for  limiting  the maximum time a caller is allowed in
        the door.  The syntax is: 

                /MAX_MINS=<minutes> 

        where "<minutes>" is replaced by a number, as in: 

                KSP-FTP scuacc.scu.edu /MAX_MINS=60 


        4.1.2 The /CONFIG Parameter       

        The  /CONFIG  parameter  is  used  in  conjunction with "dynamic"
        configuration  parameters  to  enable  or  disable  them.   For a
        complete  description  of  this  feature,  please see the section
        called "Dynamic Parameters".  













         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      22


                   CHAPTER 5 - INSTALLING YOUR ACCESS KEY     


        The  unlicensed  version of KSP FTP limits each user to a maximum
        of  five  minutes  per  session.   To remove this limit, you must
        purchase  an  access  key and install it as described below; once
        installed,  users will be limited only by their time remaining on
        the BBS.  

        There  are  three  parameters  that  must  be  specified  in  two
        environment  variables  called "KSP-ID" and "KSP-FTP" in order to
        install  your access key; the access key will not be validated if
        any parameter is missing.  

        The  environment  variable  "KSP-ID"  is used to specify your BBS
        name, as in: 

                      set ksp-id=Key Software Products BBS

        The  environment variable "KSP-FTP" is used to specify the number
        of BBS nodes and your access key separated by a semicolon as in: 

                             set ksp-ftp=2;12345678

        The  access  key  is  derived  from  the name of your BBS and the
        number   of   BBS  nodes.   The  specified  key  must  match  the
        combination  of BBS name and nodes.  If not, or if you invoke KSP
        FTP  on  a node whose node number is greater than indicated, then
        the caller will be limited to five minutes per session.  























         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      23


            CHAPTER 6 - SELECTING A SERIAL COMMUNICATION PROTOCOL    


        There  are  certain  tradeoffs  that  affect  the  selection of a
        serial  communications protocol for use with KSP FTP.  The choice
        affects   the   use  of  BBS  disk  space  and/or  file  transfer
        reliability.   After  reading  this  chapter,  you  may  wish  to
        prepare  a  bulletin  for  your users to help them understand the
        issues.  


        6.1 Internal Protocols        

        Most  serial  communications  protocols are designed with timeout
        limits  of ten seconds or less.  However, file transfers over the
        Internet  can  sometimes incur delays much greater than this, and
        affects   the   reliability   of   KSP   FTP's   internal  serial
        communications protocols.  


        6.1.1 Internal Xmodem and Ymodem Protocols     

        Most  Xmodem  and  Ymodem protocols (except the /G variants) wait
        for  an  acknowledgement  (ACK)  after each block of data that is
        transmitted.   If  the ACK does not arrive within a predetermined
        timeout  period,  the  block  is  retransmitted.  The entire file
        transfer  is  aborted  after  a  predetermined number of un-ACK'd
        retransmissions.  

        Most  implementations  of  Xmodem  and Ymodem employ a timeout of
        around  ten  seconds, but network delays can sometimes be greater
        than  this  and  can  cause  retransmission even though the first
        attempt  was received correctly.  These extra retransmissions may
        unnecessarily cause the file transfer to be aborted.  

        Some  communications  programs  offer  "relaxed timing" on Xmodem
        and  Ymodem.   This increases the timeout threshold, and may help
        if long network delays are a problem.  


        6.1.2 Internal 1K-Xmodem/G and Ymodem/G Protocols     

        The  Ymodem/G  and  1K-Xmodem/G  protocols  transmit one block of
        data  after  another  without  waiting  for  an ACK, depending on
        error-correcting  modems  for  reliability.  They work as long as
        the  receiver  can keep up with arriving data; if the receiver is
        busy  doing  something  else,  data  is  lost and the entire file
        transfer  gets corrupted.  For this reason, KSP FTP restricts the
        use  of  these  two internal protocols to downloads only; uploads



         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      24


        would fail due to occassional network delays.  


        6.1.3 Internal Zmodem Protocol       

        Network  delays  can  affect  Zmodem  uploads  the  same way they
        affect  Xmodem  and  Ymodem  as discussed above.  However, Zmodem
        downloads  are  not  affected  in  this  manner  due to a special
        feature of the Zmodem protocol.  

        Unlike  Xmodem  and  Ymodem,  Zmodem  data  blocks  are  variable
        length.     To    prevent   receiver   timeouts,   the   internal
        implementation  of  Zmodem  in KSP FTP transmits zero-length data
        blocks  during  periods of long network delay, thus resetting the
        receiver's timeout clock.  


        6.2 External Protocols        

        Downloading  a  file  using  an  external  protocol is a two-step
        process.   First  the file is transferred from the remote host to
        the  BBS  using  TCP/IP,  creating  a temporary file on the local
        disk  of the BBS.  Then KSP FTP runs the external protocol driver
        to  transfer  the  file  from  the  BBS  to  the user.  After the
        transfer  is  complete, the temporary file is deleted.  Uploading
        using an external protocol is the reverse process.  

        External  protocols  are  not affected by long time delays during
        network  transfers,  and  are  thus inherently more reliable than
        internal  protocols.   However,  since  TCP/IP transfers occur at
        very  high  rates,  temporary  disk  space  utilization  can grow
        dramatically   unless  controlled  with  the  ksp-ftp.mb_external
        configuration parameter.  


        6.3 Recommendations         

        Of  all the internal protocols, Zmodem (downloads) are by far the
        most reliable (see above).  

        If  you  are more concerned about reliability than disk space, we
        recommend  replacing  all internal protocols by external protocol
        drivers.  

        If  you  can't  afford  the  temporary  disk space, then internal
        protocols are the only choice.  

        If  you  can  afford  the  disk space, we recommend offering both
        internal  and  external  protocols,  since each type offers their



         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      25


        own  particular  benefit:  internal  protocols are faster because
        they  avoid  transfering  the  file twice, but external protocols
        are  more  reliable.   You may even choose to offer both internal
        and  external versions of the same protocols; if you do, it would
        be  appropriate to prepare a help file or bulletin to explain why
        to your users.  














































         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      26


                        APPENDIX 1 - HOW TO REACH US     


        The  Key Software Products BBS/FAX number (415-364-9847) operates
        24   hours   a   day,  7  days  a  week.   Software  at  our  end
        automatically  determines whether an incoming call is data or FAX
        and will operate accordingly.  

        If  you have access to electronic mail, you can send us a message
        via any of the following: 

        On COMPUSERVE, send mail to:

                >Internet:tech.support@ksp.com

        On PRODIGY, send mail to: VGDC59A

        On Internet, UUCP, or Bitnet, send mail to:

                tech.support@ksp.com

        On Fidonet, address mail to "UUCP" at nearest fidonet site which
        provides a gateway to Internet, such as 1:105/42.

                1st line of message: To: tech.support@ksp.com



























         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      27


                APPENDIX 2 - GETTING UPDATES VIA THE INTERNET    


        The  main  distribution  file  is KSPFTP??.ZIP, where "??" is the
        version  number.  You can retrieve this file via anonymous ftp at
        "scizzl.scu.edu",  directory "ksp".  Please note that there is no
        "e" at the end of "scizzl".  

        This  file  is also available from the KSP BBS, either by calling
        in   and   downloading,   or  via  e-mail  using  the  "LISTSERV"
        capabilities of the BBS.  

        To  use  LISTSERV,  you  must  send  a  message  addressed to the
        Internet  address  listserv@ksp.com.  The message must contain an
        LISTSERV  command  entered  as a single line of text, and it must
        be  the first line in the message. The LISTSERV commands that are
        supported include: 

        Command: HELP tlbmm-l
        Purpose: Returns an text file with help information about LISTSERV.

        Command: DIR tlbmm-l
        Purpose: Returns an e-mail message listing all of the file 
                 directories on the BBS by number and description.

        Command: LIST tlbmm-l 1
        Purpose: Returns an e-mail message listing all of the files in
                 directory #1 of the BBS.

        Command: GET tlbmm-l KSPFTP20.ZIP
        Purpose: Returns an e-mail message containing a uuencoded version of
                 the file KSPFTP20.ZIP.  To extract the file, you must save
                 the message as a file on your system, edit out the e-mail
                 header at the beginning of the file, and then use a program
                 called UUDECODE (commonly available on Unix) to convert the
                 uuencoded version back to the original ZIP format, and then
                 (finally) use PKUNZIP to extract the contents of the file.















         Copyright (C) 1995, Key Software Products. All Rights Reserved



        Aug 20, 1995            KSP FTP (tm) v2.0                      28


                         APPENDIX 3 - LEGAL STUFF       


                                LIMITED WARRANTY

        This  software  is provided 'as is' without warranty of any kind,
        either  expressed  or  implied, including, but not limited to the
        implied   warranties   of   merchantability  and  fitness  for  a
        particular  purpose.   The  entire  risk  as  to  the quality and
        performance of the program is with you.  

        Some  states do not allow the exclusion of implied warranties, so
        the  above  exclusions may not apply to you.  This warranty gives
        you  specific  legal  rights  and  you may also have other rights
        which vary from state to state.  

        Key  Software  Products  has  taken  due  care  in  preparing the
        documentation  and  software  included  in   to  ascertain  their
        correctness  and  effectiveness.   However, Key Software Products
        does  not  warrant  that  operation  of  this  software  will  be
        uninterrupted  or  error  free.   In  no event shall Key Software
        Products  be  liable  for  incidental or consequential damages in
        connection  with  or  arising out of the furnishing, performance,
        or use of this software.  


                                     LICENSE

        You  MAY  use  this software on any computer or computers in your
        possession.   The licensed version is registered for use on up to
        a  fixed  number of BBS nodes running on multiple machines and/or
        multiple multi-tasking processes.  

        You  MAY  copy this software into any machine readable or printed
        form  for  backup or modification purposes in support of your use
        of the software.  

        You  MAY  distribute  the original unmodified, unlicensed version
        of  this  software,  but you may not charge a fee exceeding $5.00
        to  cover  the  cost of duplicating, shipping, and handling.  You
        may NOT distribute a licensed version of this software.  

        You  may  NOT  use,  copy, modify, sublicense, assign or transfer
        this  software  and  its license, or any copy or modification, in
        whole  or  in  part,  except  as  expressly  provided for in this
        license.  






         Copyright (C) 1995, Key Software Products. All Rights Reserved