ÞßßßßßÝ  ÞßÝ ÞßÝ  ÞßßßßßßÝ  ÞßßßßßÝ  ÞßßßÝ  ÞßÝ  ÞßßßÝ  ÞßÝ  ÞßÝ
       Þ ÜÜÜ Ý  Þ Ý Þ Ý  Þ ÜÜÜÜ Ý  Þ ÜÜÜÜÝ  Þ   ßÝ Þ Ý  ÞÜ ÜÝ  ÞÜßÝÞßÜÝ
       Þ ßßß Ý  Þ ßßß Ý  Þ Ý  Þ Ý  Þ ßßÝ    Þ ÛÜ ßÝÞ Ý   Þ Ý    ÞÜßßÜÝ
       Þ ÜÜÜÜÝ  Þ ÜÜÜ Ý  Þ Ý  Þ Ý  Þ ÜÜÝ    Þ ÝÞÜ ßÛ Ý   Þ Ý    ÞßÜÜßÝ
       Þ Ý      Þ Ý Þ Ý  Þ ßßßß Ý  Þ ßßßßÝ  Þ Ý ÞÜ   Ý  Þß ßÝ  ÞßÜÝÞÜßÝ
       ÞÜÝ      ÞÜÝ ÞÜÝ  ÞÜÜÜÜÜÜÝ  ÞÜÜÜÜÜÝ  ÞÜÝ  ÞÜÜÜÝ  ÞÜÜÜÝ  ÞÜÝ  ÞÜÝ

                                    v3.2
             Copyright 1992,93 (c) International TeleCommunications
                             All Rights Reserved

                        BBS Phone No. 1 (314) 686-0120

                        Table Of Contents
                                i
Copyright ................................................. Page   1
-- Demo Distribution Policy -- ............................ Page   1
Hardware Requirements ..................................... Page   1
License ................................................... Page   2
Introduction .............................................. Page   3
Addressing ................................................ Page   3
   Reducing The Size Of The Nodelist ...................... Page   5
Tcp/Pc .................................................... Page   6
Installation .............................................. Page   7
   Creating Required Data Files ........................... Page   7
      Phoenix.cmd ......................................... Page   7
         Your Name ........................................ Page   7
         Mailer/Bbs Name .................................. Page   7
         Primary Domain ................................... Page   7
         Alternate Domain ................................. Page   7
         Inbound Path ..................................... Page   8
         Matrix Path ...................................... Page   8
         Requested Files .................................. Page   8
         Route Mode ....................................... Page   8
         Node Number ...................................... Page   8
         Implied Routing .................................. Page   9
         Maximum Busy ..................................... Page   9
         Secure Echomail .................................. Page   9
         Maximum Calls .................................... Page  10
         Desqview ......................................... Page  10
         Dpmi ............................................. Page  10
         Secure Address ................................... Page  12
            Outbound Calls ................................ Page  12
            Inbound Calls ................................. Page  12
         Time Between Dials ............................... Page  12
         Carrier In Delay ................................. Page  12
         Carrier Out Delay ................................ Page  12
         Shell Instructions ............................... Page  13
         Flow Control ..................................... Page  14
         Off Hook ......................................... Page  14
         Serial Port ...................................... Page  15
         Lock Rate ........................................ Page  15
         Fifo Size ........................................ Page  15
         Maximum Baud ..................................... Page  15
         Minimum Baud ..................................... Page  16
         Modem Answer ..................................... Page  16
         Modem Dial ....................................... Page  16
         Modem Out ........................................ Page  16
         Modem In ......................................... Page  16
         Modem Connect Messages And Baud Rates ............ Page  17
      Fkey.dat ............................................ Page  17
      Magic ............................................... Page  18
      Summary ............................................. Page  18
      Nodelist.dat And Domain.idx ......................... Page  19
         Ned .............................................. Page  19
         Makenl ........................................... Page  19
            Network Nodelist .............................. Page  19
            Merging Multiple Nodelists .................... Page  22
            Personal Or Private Nodelist .................. Page  23
            Including Static Data ......................... Page  24
            Hash Tables ................................... Page  24
            Other Files ................................... Page  24
      Phone.ctl ........................................... Page  24

                        Table Of Contents
                                ii
   Summary ................................................ Page  25
Phoenix Command Keys ...................................... Page  25
   Phoenix Related Keys ................................... Page  25
      Esc ................................................. Page  25
      Enter ............................................... Page  25
      ? ................................................... Page  26
      B ................................................... Page  26
      Alt-M ............................................... Page  26
         [Q]uit ........................................... Page  26
         [S]end ........................................... Page  26
         [C]rash .......................................... Page  26
         [K]ill ........................................... Page  27
         [R]oute .......................................... Page  27
         [N]ext ........................................... Page  27
      Alt-E ............................................... Page  27
      Alt-T ............................................... Page  27
      Alt-B ............................................... Page  27
      Alt-N ............................................... Page  27
      Alt-R ............................................... Page  27
      Alt-D ............................................... Page  27
      Alt-F ............................................... Page  27
      Alt-P ............................................... Page  28
      Alt-C ............................................... Page  28
      Alt-H ............................................... Page  28
      Alt-G ............................................... Page  28
      Alt-W ............................................... Page  28
      Alt-S ............................................... Page  28
      Alt-A ............................................... Page  28
   Osiris Related Functions ............................... Page  28
      Ctrl-O .............................................. Page  28
      Ctrl-T .............................................. Page  28
      Ctrl-E .............................................. Page  28
      Ctrl-L .............................................. Page  28
      Ctrl-S .............................................. Page  29
Routing Principles And Architecture ....................... Page  29
   Types Of Routing ....................................... Page  29
      Implied Routing ..................................... Page  29
      Explicit Routing .................................... Page  30
   How Implied Routing Works .............................. Page  30
      Common Questions Concerning Routing ................. Page  31
   What About Crash? ...................................... Page  33
   Implied Routing Limited ................................ Page  33
   Implied Routing Disabled ............................... Page  33
   Explicit Routing ....................................... Page  33
      Forward For {Wild-Domain Address} ................... Page  35
      No Route {Verb} ..................................... Page  35
      Send To {Wild-Domain Address} ....................... Page  36
      Route {Wild-Domain Address} To {Domain Address} ..... Page  37
      Hold {Verb} ......................................... Page  37
      Forward File {Wild-Domain Address} .................. Page  37
      Dial Delay {Seconds} ................................ Page  38
      Busy Attempts {Number} .............................. Page  38
      Maximum Connects {Number} ........................... Page  38
      Echo Processing {On/Off} ............................ Page  38
      Use Address {Domain Address} For {Domain Address} ... Page  39
      Poll {Domain Address} ............................... Page  40
      Gate {Zone} To {Domain Address} ..................... Page  40
   Examples #1 ............................................ Page  41

                        Table Of Contents
                                iii
   Example #2. ............................................ Page  41
   Example #3 ............................................. Page  42
   Common Mistake #1 ...................................... Page  42
   Common Mistake #2 ...................................... Page  42
   Tips On Speed .......................................... Page  43
Events .................................................... Page  43
   Event Lable ............................................ Page  44
   Starting Time .......................................... Page  44
   Ending Time ............................................ Page  44
   Execute On ............................................. Page  45
   Dynamic ................................................ Page  45
      Warnings ............................................ Page  45
   Explicit Route Ctrl File ............................... Page  46
   Exit Errorlevel ........................................ Page  46
   Event Batch ............................................ Page  47
   Exit On Inbound Errorlevel ............................. Page  47
   Bbs Allowed ............................................ Page  47
   Do Pick-Up ............................................. Page  47
   Maximum Request Per Event .............................. Page  47
   Summary ................................................ Page  47
Request.ctl And File Requests ............................. Page  48
   Password Protection .................................... Page  49
   Update Requests ........................................ Page  49
   Minimum Request Speed .................................. Page  49
   Requests From Unknown Systems .......................... Page  49
   Error Messages Sent To The Requester ................... Page  50
Echomail.bat .............................................. Page  50
Mail Transfer Protocols ................................... Page  51
   Xmodem/Modem7 .......................................... Page  51
   Diet Infa .............................................. Page  51
   Sealink ................................................ Page  51
      Notes On Sealink .................................... Page  51
   Wazoo .................................................. Page  52
      Turbo Charged Wazoo! ................................ Page  53
   Highspeed Mail Session ................................. Page  53
      Hsp ................................................. Page  53
         Restart Recovery ................................. Page  54
         Errors During A Transfer ......................... Page  54
      How Does This Help Me? .............................. Page  54
   Emsi ................................................... Page  55
      Outbound Emsi ....................................... Page  56
      Inbound Emsi ........................................ Page  56
      Secure Emsi ......................................... Page  56
Matrix Editor ............................................. Page  57
   Message Movement Keys .................................. Page  57
   Movement Keys, Viewing Message ......................... Page  58
   Command Keys ........................................... Page  58
      E - Enter Message ................................... Page  58
      R - Reply To Current Message ........................ Page  60
      K - Kill Current Message ............................ Page  60
      F - Forward ......................................... Page  60
      C - Carbons ......................................... Page  61
      A - Edit Current Message ............................ Page  61
      K - Kill Current Message ............................ Page  61
      F1 - Display Kludge ................................. Page  61
      F9 - Cipher Block ................................... Page  62
   Dc Word(tm) ............................................ Page  63
      Command Keys ........................................ Page  63

                        Table Of Contents
                                iv
   Cut .................................................... Page  67
   Paste .................................................. Page  67
   Quick Jump ............................................. Page  68
   Macro Keys ............................................. Page  68
Service Requests .......................................... Page  69
   Programmers Notes ...................................... Page  71
Nodelist Editor ........................................... Page  71
   Add .................................................... Page  73
   Find ................................................... Page  73
Log File .................................................. Page  74
Errorlevels & Error Msgs .................................. Page  74
Human Callers ............................................. Page  75
Smart(tm) Packer .......................................... Page  76
   Maximum Number Of Outbound Messages .................... Page  77
Phoenix.sav ............................................... Page  78
Alternate Domains ......................................... Page  78
   Phoenix.aka ............................................ Page  78
   How To Pickup Mail When Multiple Domains Are Involved .. Page  79
Busy The Modem ............................................ Page  80
Auto Detecting Osiris Bbs Software ........................ Page  80
   Disabling The Shell .................................... Page  81
Testing Your Setup ........................................ Page  81
Aborting .................................................. Page  81
Tic ....................................................... Page  81
Raid ...................................................... Page  82
Areafix ................................................... Page  82
   Afix.bat, Tic.bat, Raid.bat, Echomail.bat .............. Page  82
Master Transfer Timer ..................................... Page  83
Msg Storage Format ........................................ Page  83
Security Systems .......................................... Page  87
   Secure  Address ........................................ Page  87
   Session  Level  Password ............................... Page  88
   System  Level  Password ................................ Page  88
   Require Pwd For Mail Pickup ............................ Page  88
Port.dat .................................................. Page  89
Serial Drivers And Multi-Port Cards ....................... Page  90
   Intelligent Multi-Port Stargate ........................ Page  90
   Intelligent Multi-Port Arnet ........................... Page  91
   Intelligent Multi-Port Digiboard ....................... Page  91
   Fossil ................................................. Page  92
   Non-Intelligent Serial Cards ........................... Page  92
   Non-Intelligent Digiboards ............................. Page  92
      Setting Up  The Digi Pc/4 Board ..................... Page  93
         Setting The Jumpers .............................. Page  93
         Multi-Board Connectors ........................... Page  94
         Dip Switches ..................................... Page  94
      Setting Up A Digiboard Pc/8 ......................... Page  95
         Setting The Jumpers .............................. Page  95
         Multi-Board Connectors ........................... Page  96
         Dip Switches ..................................... Page  96
      Setting Up The Digiboard Pc/16 ...................... Page  97
   Non-Intelligent Stargate ............................... Page  99
   Non-Intelligent Ast .................................... Page  99
   Non-Intelligent Boca ................................... Page 100
8259 Interrupt Management ................................. Page 100
Phoenix Interactive Terminal Module ....................... Page 101
   Mouse Commands ......................................... Page 101
   Hotkey ................................................. Page 101

                        Table Of Contents
                                 v
   Individual Options ..................................... Page 101
      Download ............................................ Page 102
      Upload .............................................. Page 102
      Protocols ........................................... Page 102
      Download Clipboard .................................. Page 103
      Upload Clipboard .................................... Page 106
      Send Log-In String .................................. Page 109
      Screen Snapshot ..................................... Page 109
      Paste From File ..................................... Page 109
      Information ......................................... Page 110
      Shift F1 Throught Shift F10 ......................... Page 110
      Alt F1 Throught Alt F10 ............................. Page 110
      Mouse Screen Cut .................................... Page 111
   Phone Book ............................................. Page 111
      Bbs Name ............................................ Page 112
      Bbs Phone Number .................................... Page 112
      Predial String ...................................... Page 112
      Default Protocol .................................... Page 112
      Log-On Macro ........................................ Page 113
      Connect Time ........................................ Page 113
      Times Called ........................................ Page 113
      Last Called ......................................... Page 114
      Uart Settings ....................................... Page 114
      Duplex .............................................. Page 114
      Logfile ............................................. Page 114
      Autolog ............................................. Page 114
      File Separation Method .............................. Page 115
   Downloading And Auto-Virus Scanning .................... Page 115
   Terminal Emulation ..................................... Page 116
   Keyboard ............................................... Page 116
   Script Language ........................................ Page 117
   Call.log ............................................... Page 118
   Filebox ................................................ Page 118
   Dialing ................................................ Page 118
Advanced Operations ....................................... Page 118
   Nomail ................................................. Page 118
   Recycle.xxx ............................................ Page 119
   Sysdown.xxx ............................................ Page 120
   Special Phoenix Flag Settings .......................... Page 121
   Crash = Direct ......................................... Page 121
   Netcom.exe ............................................. Page 121
      Wait <Node #> ....................................... Page 122
      Shutdown <Node #> ................................... Page 122
      Recycle <Node #> .................................... Page 122
      Free <Node #> ....................................... Page 122
      Nomail <Node #> ..................................... Page 122
      Copy <Node #> ....................................... Page 122
      Move ................................................ Page 122
      Netcom.cfg .......................................... Page 122
      Netcom2.cfg ......................................... Page 123
Screen Blanker ............................................ Page 127
Robot ..................................................... Page 128
Getting A Test Drive Key .................................. Page 129
   Test Drive Mode ........................................ Page 129
   Bbs Front End Mode ..................................... Page 129
Price ..................................................... Page 129
Technical Support ......................................... Page 130

                        Table Of Contents
                                 vi
File Structures ........................................... Page 130
   Matrix Message Header .................................. Page 130
   Phoenix.cmd ............................................ Page 132
   File Requests .......................................... Page 133

         Phoenix           Technical Reference Manual        Page   1

                                   Copyright
 
         Despite the method of marketing, Phoenix is not in the public  
         domain nor is it SHAREWARE.  Phoenix is a proprietary product  
         of  International  TeleCommunications, protected  under  U.S.  
         copyright  law,  International treaty provisions,  and  trade  
         secret laws of general applicability.

          
         Copying, duplicating, selling or otherwise distributing  this 
         product,   except   as  expressly  permitted  in   the   DEMO 
         Distribution  Policy  is a violation of the  Law.   You  are, 
         however,  granted the right, in fact encourage, to  make  and 
         distribute  copies  of the DEMO version, with  the  following 
         provisions.
 
                        -- Demo Distribution Policy --
 
          1.   Feel  free  to distribute the DEMO  version  as  often 
               as you like. 
          2.   Please do not distribute the program without all of its 
               original files. 
          3.   You  must get written  permission  before  distributing 
               Phoenix with any "Bundled" software packages. 
          4.   You may NOT accept payment for the program.  A  copying 
               fee   of  10.00  per  diskette  may  be  charged   when 
               distributed by a non-profit user-group. 
          5.   You may NOT alter the program or documentation  in  any 
               way. 
          6.   Individuals,   groups,  vendors,  or   other   software 
               distribution companies who market diskettes  containing 
               the  DEMO or SHAREWARE programs for profit must  NOTIFY 
               us, in writing, 30 days before distribution.
 
                             Hardware Requirements
 
         The  following  list represents  the   minimum  configuration   
         your   system  should  have  to   maximize  the potential  of  
         the program.
 
          -    IBM Personal Computer (or true compatible)  with  384K 
               (minimum)     RAM,    296K   free   for   Phoenix.    I    
               suggest,  although    it is  NOT  required,   1 Meg  of   
               AST   EEMS 3.20 or LIM 4.00 RAM
          -    PC-DOS  or  MS-DOS, Ver. 3.0 or  later. 
          -    A Hard Disk Drive is recommended  but you can use a 1.2 
               Meg Floppy Disk.
          -    Asynchronous communications (serial port) adapter 
          -    RS-232 cable with the standard nine pins connected (some 
               modem cables do not have all the pins hooked-up). 




         Phoenix           Technical Reference Manual        Page   2

          -    Intelligent AT command set modem 
          -    Eighty column color monitor. 
          -    Voice-grade  telephone  connection for modem. 
          -    Intel  Compatible  286, 386,  486,  or  Pentium CPU. 
          -    Two or THREE button mouse.
 
                                    License
 
         1.  License Grant. International  TeleCommunications  grants, 
         when  registered, to you a non-exclusive license to  use  one  
         copy   of   Phoenix  on a single computer or  on   a   single   
         terminal  connect  to a single computer.  Neither  concurrent  
         use on  two or  more  computers  nor  use in  a  local   area   
         network   is authorized without advanced written  consent  of   
         International   TeleCommunications   and   the  payment    of   
         additional  license fees.

         2. International TeleCommunications' Rights. You  acknowledge 
         and   agree  that  Phoenix  is  a  proprietary   product   of   
         International  TeleCommunications,    protected   under   U.S   
         copyright   law, international  treaty  provisions, and trade  
         secret    laws    of  general  applicability.   You   further  
         acknowledge  and agree that all  rights, title, and  interest  
         in  and to Phoenix are and  shall remain  with  International  
         TeleCommunications.
 
         3. Other Restrictions. You may not lease or rent Phoenix. You  
         may not disassemble, decompile, or reverse engineer Phoenix.

         4.   Phoenix   is  licensed  "AS   IS,"   and   International  
         TeleCommunications disclaims any and all warranties,  whether  
         express  or  implied,  including   (without  limitation)  any  
         implied  warranties  of   merchantability or  fitness  for  a  
         particular purpose.

         5. Limitation of Liability. International TeleCommunications'  
         cumulative  liability to you or any other party for any  loss  
         or  damage  resulting from any claims,  demands,  or  actions  
         arising out of or relating to this agreement shall not exceed  
         the license fee paid to International TeleCommunications  for  
         the  use  of  Phoenix.  In  no  event  shall    International  
         TeleCommunications  be liable for any  indirect,  incidental,  
         consequential, special, or exemplary damages or lost profits,  
         even if International TeleCommunications has been advised  of  
         the possibility of such damages. Some states do not allow the  
         limitation  or  exclusion  of  liability  for  incidental  or  
         consequential  damages, so the above limitation or  exclusion  
         may not apply to you.






         Phoenix           Technical Reference Manual        Page   3
 
         6.  Governing Law. This license agreement shall be  construed 
         and  governed  in accordance with the laws of  the  State  of 
         Missouri.
 
         7. Severability. Shall any term of this license agreement  be 
         declared  void  or unenforceable by any  court  of  competent 
         jurisdiction,  such declaration shall have no effect  on  the 
         remaining terms hereof.
 
                       International TeleCommunications 
                                 302 Mckinley 
                       Poplar Bluff, Missouri USA 63901

                                 Introduction

         Phoenix was designed to:

         1)  Be physically small and to consume as little  memory  and  
         disk space as possible.

         2) Be exceptional FAST in respects to mail sessions and  file  
         transfers.

         3) EASY to set-up and use.

         4) Have a very Sophisticated and Intelligent IMPLIED  routine  
         manager.

         5)  Have  a very flexible and easy to  use  EXPLICIT  routing  
         system.

         6)  Intelligently  handle multiple domains  without  operator  
         intervention.

         Phoenix was NOT designed to be or do everything for everyone.

                                  Addressing

         Before  you  can  INSTALL Phoenix,  you  have  to  understand  
         the ADDRESSING system Phoenix uses.

         Internet  uses  an addressing system based on NET  and  NODE.  
         Those of you that have had experience in Fidonet will  notice  
         this is similar to the Fidonet NET and Node concept. 

         In  fact they are almost identical which leads us to  beleive  
         Tom  Jennings,  founder  of  Fidonet,  used  Internet  as   a  
         model for Fidonet.






         Phoenix           Technical Reference Manual        Page   4

         Fidonet uses a 16 bit unsigned integers, an integer is a non- 
         decimal  number,   for the NET and a 16 bit integer  for  the  
         NODE. This number can hold values ranging from 0 to 65535. 

         Internet  uses 4 different classes of NET and  NODE  numbers.  
         The  class  differs based on the number of NODEs  within  the  
         NET. The mechanics of how this works is not important, but is  
         fascinating if you are a programmer. 

         An Internet address takes the form of 123.12.12.21, a  period  
         is  used to break the NET and NODE into 4 8 bit chunks.  This  
         is  an address that is used on the  Software/Hardware  level.  
         The  PERSON entering the address would not enter it  in  this  
         format.  They would enter something like  Jones@beta.GOV  and  
         the software would translate that to the Internet address. 

         Jones@beta.GOV  is  a  label. It is  easier  to  associate  a  
         person's  address to a label than the Internet address.  When  
         you   enter  a  message  to  Jones@beta.GOV,   the   software  
         translates  that label to an Internet address. You don't  see  
         or even know the translation is going on. 

         Personal  Computers  generally don't have the disk  space  to  
         store  the information required to resolve large  numbers  of  
         LABELS. That is one of the reasons most Fidonet mail programs  
         require  you to enter the NET and NODE numbers instead  of  a  
         label.
         
         Internet  does suffer from one major flaw. It  doesn't  allow  
         for  individual machine addresses. Since all the machines  in  
         Internet   are  hooked  together  in  network  fashion,   the  
         addressing system doesn't need to go that low.

         A  Fidonet  address is based on individual machines  and  the  
         NODE number references a single machine.

         Although  the Fidonet format does provide for a large  number  
         of systems, every NODE must keep a very large list,  commonly  
         referred  to as a nodelist, of NETS. If Fidonet were to  grow  
         to the maximum number of NETS, each NODE would have to keep a  
         minimum of 65535 entries in their nodelists.

         Another problem, Fidonets addressing method  doesn't  provide  
         for  the possibility that other, totally different,  NETWORKS  
         exist.

         Example:  Fidonet, a GROUP of NETS bound together to format a  
         Network  of individual systems, cannot co-exist  with  Family  
         Net,  another  Network  of  individual  systems.  Since  both  
         networks  use the same NET/NODE addressing system, 100.10  in  
         Fidonet would conflict with 100.10 in Family Net.



         Phoenix           Technical Reference Manual        Page   5

         Those  developing  mailers for  use within Fidonet  have,  in  
         recent years, attempted to find ways around this by  kludging  
         the use of ZONE. 

         E.g., ZONE.NET.NODE

         However, Fidonet has never OFFICIALLY adopted the use of ZONE  
         as  part  of an address. They use it in  their  NODELIST  and  
         offer  an  OPTIONAL, if it is optional it might as  well  not  
         be  there, mail packet header that has this field, but it  is  
         not part of the official specifications.

         Several NETWORKS use the ZONE field to co-exist. Some  within  
         Fidonets   frown  on that concept and believe a  ZONE  should  
         only be used to separate geographic regions. 

         Whether it is used to separate systems by geographic location  
         or by Network location isn't important, in fact it is just  a  
         matter  of  semantics. The results are  identical,  the  ZONE  
         number provides a GATEWAY to other geographic locations or to  
         other NETWORKS. 


                         Reducing The Size Of The Nodelist

              The only way you can reduce the size of the nodelist  is  
              to  reduce  the number of REQUIRED entries. One  of  the  
              ways  to do that is to subdivide the NODE and produce  a  
              POINT.

              We now have the format of; zone.net.node.point and  this  
              is  the  format Phoenix uses. Funny if you look  at  it,  
              Internet  was the model for Fidonet and now  we've  come  
              full circle and we're back to internet 4-D addressing. 

              Anyway,  the  entire address is called  a  DOMAIN,  each  
              section of the DOMAIN address is called a subdomain. The  
              period  is used to divide the different  subdomains.  

              If  you  are  use to  seeing  1:245/405.0,   the  colon,  
              forward  slash, and period  are not actual part  of  the  
              address.  They are used to divide the subdomains. It  is  
              really up to the software you're using and Phoenix using  
              the  period  to reduce coding overhead.  Do  NOT  forget  
              this.  ANYTIME  ANY  Phoenix application,   asks  for  a  
              Domain address it expects you to use a PERIOD to  divide  
              the subdomains. What about @, doesn't internet use that?  
              It  does, but that references a particular PERSON  on  a  
              machine. We don't really need that since we have the  TO  
              field  in  the matrix message and BBS software  that  is  
              capable  of taking the TO field and routing it  to  that  
              persons mail box.


         Phoenix           Technical Reference Manual        Page   6


              You have no doubt seen several Fidonet mailers make  use  
              of or rather MISUSE of @. Keep in mind that most Fidonet  
              developers   are  not  professional   TeleCommunications  
              developers  and do not fully understand the  concept  of  
              domain addressing. And what they do not understand, they  
              tend to twist into what they think it should mean.

              The  ZONE.NET.NODE.POINT  addressing system  also  means  
              you're never likely to run out of unique address. 
 
              There are so many unique addresses available, you  could  
              assign  every man, women, and child on the face of  this  
              planet an address and have plenty left over.

              To  top  it off, we now have an addressing  method  that  
              supports the concept that no individual systems needs to  
              keep  EVERYONE listed in their nodelist. They only  HAVE  
              to  keep  the system directly above  them  and  directly  
              below them.

              Again, those developing mailers for  use within  Fidonet  
              have,  in  recent years, attempted to find  ways  around  
              this same problem by kludging the use of POINT. 

              And  like  the  ZONE,  Fidonet  has  never  adopted  any   
              standards  for  the use of POINT. In fact,  it  is  only  
              referenced twice in Fidonet Technical Specifications and  
              only as kludge line options in messages.

              What  this  really boils down to is the fact  that  ZONE  
              and  POINT addressing is fairly SOFTWARE specific.  Each  
              mailer  handles  it slightly different.  Fidonet  should  
              really UPDATE their technical specifications and  change  
              the "OPTIONAL" fields in the messages to REQUIRED so  we  
              can  all standardize our .MSG and .PKT formats so  third  
              party  developers would can make one utility  that  will  
              work with all mailers.

                                       Tcp/Pc

              TCP/PC  simply means 4-D networking. TCP/PC and  Fidonet  
              different in several areas.

              1.  TCP/PC is 4-D, Fidonet is 2-D. This is based on  the  
                  OFFICAL  technical specifications provided  by  each  
                  network. While some Fidonet applications do  support  
                  4-D addressing, to some degree, 4-D is not  required  
                  nor OFFICAL. Fidonet also uses 2-D routing.
              2.  TCP/PC supports FULL file routing, Fidonet does not.
              3.  TCP/PC supports routing to the ZONE level,  Fidonet  
                  does not.


         Phoenix           Technical Reference Manual        Page   7

              Because  their  are some major differences  in  the  way  
              routing  is handled between fully integrated 4-D  TCP/PC  
              networks  and  2-D Fidonet style networks,  the  IMPLIED  
              routing system must be told which to use.

                                 Installation

                            Creating Required Data Files

                                       Phoenix.cmd

                   Phoenix.cmd   contains   information   about   your  
                   particular   installation.  Information   such   as  
                   address, directories, modem strings, serial  ports,  
                   etc.  and you create and maintain Phoenix.cmd  with  
                   the program CONFIG.EXE.

                   Warning, config.exe DOES REQUIRE a mouse. If you do  
                   not  have  a  mouse  installed,  do  NOT  run  this  
                   program.

                   To  EDIT  any field, move the mouse cursor  to  the  
                   field and click the LEFT mouse button.

                   Some  of the fields are TOGGLE fields,  to  prevent  
                   you from entering an illegal value. A TOGGLE  field  
                   will  CYCLE to the NEXT available setting when  you  
                   CLICK on it.

                   To select an option from one of the menus, move the  
                   mouse  cursor  to that option and  click  the  LEFT  
                   mouse button.

                                          Your Name

                        This  is YOUR name, generally first and  last.  

                                       Mailer/Bbs Name

                        This  is the NAME you have selected  for  your  
                        mail site.
                                        Primary Domain

                        This  is  your  address,   ZONE.NET.NODE.POINT  

                                       Alternate Domain
                                          (OPTIONAL)

                        You  can  define  up to  53  alternate  DOMAIN  
                        addresses.    Three   here   and   50    using  
                        Phoenix.aka, see section on ALTERNATE  DOMAINS  
                        for details.


         Phoenix           Technical Reference Manual        Page   8

                                         Inbound Path                                   

                        This  tells  Phoenix WHERE to  place  incoming  
                        FILES, ECHOMAIL, PKT's (matrix messages),  and  
                        other items during a mail session.

                                         Matrix Path

                        This  should  point  to  the  directory   that  
                        contains  your matrix messages and you  SHOULD  
                        end the path with a backslash. 

                                       Requested Files
                                          (OPTIONAL)

                        This  is  the name of the file  to  send  when  
                        someone file requests FILES.

                        Phoenix  will replace FILES with the  name  of  
                        the  file  you define in this field  and  then  
                        Phoenix will search the directories listed  in  
                        REQUEST.CTL in an attempt to find it.

                                          Route Mode

                        The  IMPLIED  Route  Manager  has  TWO  modes,  
                        TCP/PC and FIDONET.

                        TCP/PC  mode  means Phoenix  will  attempt  to  
                        resolve  an address even if it has to  go  all  
                        the way to the zone level.

                        However, Fidonet doesn't support routing  that  
                        goes that HIGH. Switching to FIDONET mode will  
                        cause the IMPLIED route manager to STOP on the  
                        highest level Fidonet supports.

                                       Node Number
                                          (OPTIONAL)

                        Several  multiple line BBS programs require  a  
                        NODE number on the command line, Osiris does.

                        If you are using the SHELL method  to call the  
                        BBS  and  you need to pass  the  NODE  number,  
                        Phoenix  will  use the  number found  in  this  
                        field. 

                        For information on HOW to get the node  number  
                        INCLUDED,   read   the   section   on    SHELL  
                        INSTRUCTIONS



         Phoenix           Technical Reference Manual        Page   9

                                       Implied Routing

                        This  determines the TYPE of  IMPLIED  routing  
                        Phoenix  will use and your options  will  vary  
                        depending on the ROUTE MODE.

                        DEFAULT, use FULL TCP/PC Implied Routing. That  
                        includes  routing  FILES, ECHOMAIL,  and  FILE  
                        REQUESTS

                        LIMITED, do not route anything that has a file  
                        attach.

                        DISABLED, turns Implied routing OFF.

                        If  the  ROUTE MODE is  "FIDONET",  your  only  
                        options are LIMITED and DISABLED.

                        If  the  ROUTE  MODE is  "TCP/PC",  all  three  
                        options will be made available.

                                         Maximum Busy

                        This determines the MAXIMUM number (between  1  
                        and  255)  of busy signals you  can  get  when  
                        calling an individual system during a specific  
                        event.  Once  you reach  the  maximum  number,  
                        Phoenix will stop calling. This is reset  when  
                        you change events.

                                       Secure Echomail
                                          (OPTIONAL)

                        This   prevents  anyone  from   dropping   off  
                        echomail  unless their NODELIST.DAT  "ECHOMAIL  
                        ALLOWED" flag is turned on.

                        This is the ONLY method of running 100 percent  
                        secure echomail.

                        Phoenix  handles this by ALLOWING them  to  do  
                        the physical file transfer but as soon as  the  
                        transfer has finished, it will promptly delete  
                        the   file  if  they  do  NOT  have   echomail  
                        authorization. 

                        It  is recommended that you use SESSION  level  
                        passwords   with  ANYONE  that  has   echomail  
                        authorization. 





         Phoenix           Technical Reference Manual        Page  10

                                        Maximum Calls

                        This determines the MAXIMUM number (between  1  
                        and  255)  of calls to  an  individual  system  
                        during  a specific event. Once you  reach  the  
                        maximum  number,  Phoenix will  stop  calling.  
                        This is reset when you change events.

                        A  CALL is registered when you get a  physical  
                        CONNECT  to the system, mail does NOT have  to  
                        be  transferred.  If  the  system  is   having  
                        problems,  software  or  hardware,  this  will  
                        prevent  you  from running up  a  large  phone  
                        bill. I would suggest that you keep this  low,  
                        no more than 10.

                                           Desqview
                   
                        While  Desqview can be detected  by  searching  
                        memory  for  a  specific  signature,   several  
                        NETWORK  programs use the same  signature.  To  
                        avoid  confusion, we ask that you TELL  us  if  
                        you have or do not have Desqview installed.

                                             Dpmi

                        This  determines  *IF* Windows or  OS-2  DPMI  
                        time slicing will be used.

                        While  time slicing does reduce the  drain  on  
                        your  CPU  it may, depending  your  system  or  
                        hardware, greatly reduce transfer rates. 

                        Despite the term "Multitasking",  multitasking  
                        is impossible using a single CPU. The CPU  can  
                        only  process a single instruction (2  integer  
                        instructions if the new Intel P5 chip is used)  
                        at  once.  Multitasking with a single  CPU  is  
                        nothing more than quickly swapping in and  out  
                        programs giving each a short period of time to  
                        run before swapping in another one. 

                        For  instances,  when Windows  swaps  away  it  
                        freezes  everything in that windows  and  this  
                        includes  ANY  device  drivers  or   interrupt  
                        service  routines.  If you  use  the  internal  
                        serial driver, it to is frozen and cannot send  
                        data that may be in the transmit buffer. 






         Phoenix           Technical Reference Manual        Page  11

                        While all multitaskers do this, some are  more  
                        efficient   than   others.  Some   will   give  
                        interrupt services higher priority than  other  
                        tasks  and  allow them to use  much  more  CPU  
                        time. Even if the application only gets access  
                        to  the CPU once ever oh . . . 9  clock  tics,  
                        interrupt  routines used by  that  application  
                        may get access to the CPU every 2 clock  tics.  
                        This  is  sometimes  referred  to  as   multi- 
                        threading. 

                        There  are conditions when it  doesn't  matter  
                        how  the  multitasker  works.  For  instances,  
                        intelligent serial cards.

                        If  you  have an intelligent serial  card,  it  
                        handles  sending the data and the  multitasker  
                        does not stop it from doing so by swapping out  
                        the window. In this case, always use DPMI Time  
                        Slicing.

                        Fossil  drivers can sometimes get around  this  
                        if  they  are loaded BEFORE  the  multitasker.  
                        However, some multitaskers will not allow dual  
                        access, from different windows, to the fossil.

                        Testing  is the only way to determine if  your  
                        system works better with or without DPMI  time  
                        slicing.

                        Send and recive files using DPMI time  slicing  
                        and  without DPMI time slicing. If you  run  a  
                        single node, compare the transfer rates.

                        If  you  run  multiple  nodes,  it  gets  more  
                        involved.  After  getting  the  first  set  of  
                        figures,  repeat the entire process  but  make  
                        sure  you have someone doing the  uploads  and  
                        downloads  on ALL the other nodes at the  same  
                        time  THEN  compare ALL  the  transfer  rates.  

                        Doing  multiple transfers at once DOES  effect  
                        the outcome. You may find that while  transfer  
                        rates drop drastically when only one  transfer  
                        is going on, they may actually go up when  you  
                        have multiple transfers going at once.

                        When  you  are doing the tests, keep  in  mind  
                        that  transfer  rates WILL vary,  but  only  a  
                        little  bit. Look for the big differences  and  
                        don't worry about 1 to 3 percent.



         Phoenix           Technical Reference Manual        Page  12

                                        Secure Address
                                          (Optional)

                        Engages  secure  addressing.  
                                          Outbound Calls 

                             When  you  place an  outbound  call  with  
                             SECURE  ADDRESSING  turned  ON,   Phoenix  
                             matches the remote systems DOMAIN address  
                             with the one that triggered the call.  If  
                             they do not match, Phoenix hangs UP.

                             This prevents mail from being sent to the  
                             wrong  location  due to an error  in  the  
                             network NODELIST.xxx or an error in  your  
                             PHONE.CTL file.

                                           Inbound Calls

                             When  you  receive an  inbound  call  and  
                             secure  addressing is turned on,  Phoenix  
                             will  HANG-UP if the callers NOT  in  the  
                             nodelist.dat file.

                             This  prevents  TERMINAL  programs   with  
                             WAZOO  emulation systems  from  bypassing  
                             BBS   download  restrictions   via   file  
                             requests.  Something that is starting  to  
                             become a problem.

                                      Time Between Dials

                        This determines the number of SECONDS  Phoenix  
                        will wait between outbound dial attempts. 

                                       Carrier In Delay

                        This determines the NUMBER of SECONDS  Phoenix  
                        will wait for an INBOUND connect once RING has  
                        been reported by the modem. SECONDS should  be  
                        ONE   second  longer  than  your   modems   S7  
                        register.

                                      Carrier Out Delay

                        This determines the NUMBER of SECONDS  Phoenix  
                        will  wait  for an OUTBOUND connect  once  the  
                        DIALING  process has been  completed.  SECONDS  
                        should  be ONE second longer than your  modems  
                        S7 register.




         Phoenix           Technical Reference Manual        Page  13

                        You  should set this, and the S7 register,  to  
                        at least 45 if you have a v32,v32bis,HST, PEP,  
                        or any other high-speed modem.

                        If you are placing overseas calls, you  should  
                        set  this and the S7 register to at least  60.  
                        75 if used with a high-speed modem.

                                      Shell Instructions
                                          (OPTIONAL)

                        If you would rather have Phoenix SHELL to  the  
                        BBS instead of exiting with an errorlevel, use  
                        this  field.  If you are running  Osiris,  see  
                        section  on  AUTO-DETECT  before  using   this  
                        option.

                        Your  COMMAND LINE should contain the NAME  of  
                        the  program  along  with  any  command   line  
                        arguments, maximum length is 50 characters.

                        You have several reserved character  sequences  
                        that  you can include to pass baud rate,  lock  
                        rate,  serial port number, and time to end  of  
                        event.

                        *B  -  Phoenix  will  replace  this  with  the  
                        CONNECT baud rate.

                        *P - Phoenix will replace this with the serial  
                        port number you're on.

                        *L   -  Phoenix  will replace  this  with  the  
                        LOCKED SERIAL rate.

                        *T  - Phoenix will replace this with the  time  
                        to end of event, in minutes.

                        *N   - Phoenix will replace this with the  BBS  
                        Node  number  you  defined  using  the   "NODE  
                        NUMBER" label. 

                        SHELLING  to the BBS is the  preferred  method  
                        for two reasons.

                        1.  You're  matrix area does not  have  to  be  
                        rescanned.  

                        2.  It  is just plain faster and  easier  than  
                        setting up errorlevels in a batch file. 




         Phoenix           Technical Reference Manual        Page  14

                        When you SHELL to the BBS, Phoenix will  shift  
                        to  EMS or overlay itself to DISK to give  the  
                        BBS  all  of your  machines  original  memory,  
                        minus 5K.

                        Phoenix   does  NOT  change  into   the   BBS'  
                        directory.  If  you're running  Phoenix  in  a  
                        different directory, SHELL to a batch file and  
                        have  the  BATCH  file  change  into  the  BBS  
                        directory.

                        Phoenix  will LOG the shell command  line,  to  
                        the  Phoenix  log, that it used  to  call  the  
                        application.  This  gives you a way  to  DEBUG  
                        your SHELL command line.

                        Phoenix  will  also tell you, in  the  Phoenix  
                        log, if NO application was executed during the  
                        SHELL.

                        SHELL INSTRUCTIONS OSIRIS -B*B -P*P -T*T -N1

                                         Flow Control

                        You  have  TWO  options;  CTS  hardware   flow  
                        control and RTS/CTS hardware flow control.
 
                        In  most cases CTS is  best. However,  if  you  
                        are  running  Phoenix on a  Network  or  under  
                        Desqview, Windows, or OS/2 you may need to use  
                        RTS/CTS.

                        If  RTS/CTL  is used, Phoenix will  lower  RTS  
                        when  it opens, reads from, writes  to,  moves  
                        the file pointer to a new position, and closes  
                        a  file. Lowering RTS lets the modem know  the  
                        computer  is  NOT ready to receive  data.  The  
                        modem will store the data internally until RTS  
                        is high.

                        RTS/CTS  does slow down transfers and you  can  
                        STILL  get errors if RTS is held low  for  TOO  
                        long and the modem runs out of storage space.

                                           Off Hook

                        This  tells Phoenix how to handle  your  modem  
                        when  you exit. If OFF HOOK is turned ON,  the  
                        modem will come OFF HOOK, giving a busy signal  
                        to anyone that attempts to call.

                        If  OFF HOOK is turned OFF, Phoenix will  DROP  
                        DTR.

         Phoenix           Technical Reference Manual        Page  15

                                         Serial Port

                        Tells Phoenix which serial port to use.  Valid  
                        ports range from 1 - 33. 

                                          Lock Rate
                                          (OPTIONAL)

                        This  tells Phoenix to FIX the serial port  at  
                        this baud rate. When you connect with  another  
                        mailer or a HUMAN calling for the BBS, Phoenix  
                        will NOT change the serial baud rate. It  will  
                        simply allow the MODEM to handle adjusting the  
                        SEND/RECEIVE speeds. 

                        Phoenix will NOT pass this rate as the CONNECT  
                        baud  rate.  It will pass the rate  the  modem  
                        returns in the CONNECT message.

                        If  you LOCK the serial rate higher than  9600  
                        baud you MUST have a 16550 Uart. Attempting to  
                        run with a LOCKED serial rate higher than 9600  
                        will  almost always generate errors  when  you  
                        attempt to RECEIVE very large files, generally  
                        over 50K in size).

                                          Fifo Size

                        Phoenix  will automatically detect and  use  a  
                        16550 Uart. 

                        You  have  to tell Phoenix how many  bytes  to  
                        send per TX interrupt. This is a TOGGLE  field  
                        and you can TOGGLE between 2, 4, 6, 8, 10, 12,  
                        , 14 and 16.

                        If  you have a slower computer,  your  running  
                        under  Desqview-OS/2-Windows, or on a  network  
                        you  may need to raise this to 10 or  more.  

                                         Maximum Baud

                        This  is  the  maximum baud  rate  your  modem  
                        supports  and  the serial  port  is  initially  
                        opened to this rate. 

                        If you have a LOCKED serial port, use 9600  in  
                        this  field. A LOCKED serial port  is  treated  
                        differently  and Phoenix will use the  MAXIMUM  
                        BAUD field as an internal storage variable.




         Phoenix           Technical Reference Manual        Page  16

                                         Minimum Baud

                        This is the minimum baud rate you are  willing  
                        to accept on inbound calls. Phoenix will hang- 
                        up if the CONNECT is less than this value.

                   After  you have filled out all the fields on   THIS  
                   screen,  move your mouse cursor to the BOX  labeled  
                   "MODEM" and click the LEFT mouse button.

                   This will open another screen containing the  Modem  
                   STRINGS and CONNECT messages for YOUR modem.


                                         Modem Answer
                                          (OPTIONAL)

                        This is the command string you want Phoenix to  
                        send to the modem when the modem reports RING,  
                        on incoming calls.

                        If  your modem is set to AUTO-ANSWER,  do  NOT  
                        use  this  field. If you do,  the  modem  will  
                        simply NOT answer the phone.

                                          Modem Dial

                        This is the command string you want Phoenix to  
                        send to your modem to get it to DIAL the phone  
                        number. Generally this is ATDT or ATDP.

                                          Modem Out

                        This  is the command string that prepares  the  
                        modem  for an outbound call. It is sent  PRIOR  
                        to  the  NODELIST PERDIAL STRING and  the  MDM  
                        DIAL string. If your modem requires a carriage  
                        return,  most  do but a few do  not,  end  the  
                        string with the vertical bar, |

                                           Modem In

                        This is the command string sent to your  modem  
                        to get it ready to ANSWER incoming calls.  The  
                        string  should  set  your  modem  so  that  it  
                        returns  VERBOSE response codes and  does  NOT  
                        echo commands. If you see something like:

                        Huh?  <ATH0E0V1>  then your modem  is  echoing  
                        commands. Although Phoenix can handle this, it  
                        does  slow  things down because it  will  keep  
                        trying until it gets OK from the modem.


         Phoenix           Technical Reference Manual        Page  17

                        If your modem requires commands to end with  a  
                        carriage return, most do but a few do not, end  
                        the string with the vertical bar, |

                            Modem Connect Messages And Baud Rates

                        Phoenix  lets  you  define up  to  50  CONNECT  
                        messages   along  with  the  serial  rate   to  
                        associate with the message.

                        Each   CONNECT  message  can  be  up   to   50  
                        characters long. 

                        The BAUD rate can be any legal serial rate you  
                        want Phoenix to use for that connect message.

                        CONFIG  will  automatically fill in  the  MOST  
                        popular  CONNECT messages and BAUD rates  when  
                        you run it for the first time.

                        To reach the CONNECT fields 20 - 50, click  on  
                        the PAGE DOWN BOX.

                        When you finish filling out the MODEM Strings,  
                        CONNECT  messages,  and baud  rates  click  on  
                        RETURN. 
                                        Fkey.dat

                   FKEY.DAT  contains information about F1 though  F10  
                   and  any  programs you may have defined  for  those  
                   keys.

                   If    FKEY.DAT   is   missing,   CONFIG.EXE    will  
                   automatically  create  it as soon as  you  ran  the  
                   program.

                   While you don't have to actually DEFINE anything at  
                   this  point,  we'll talk about it because it  is  a  
                   required file, as far as PHOENIX.EXE is  concerned.  

                   To  reach  the F-KEY definition  system,  move  the  
                   mouse cursor to the BOX labeled FKEYS and click the  
                   LEFT mouse button.

                   To  define a KEY, move to the mouse cursor  to  the  
                   field  labeled F1, F2, F3, etc. and click the  LEFT  
                   mouse  button. Then enter the NAME of  the  program  
                   along with any command line information.






         Phoenix           Technical Reference Manual        Page  18

                                          Magic

                   Phoenix lets you define up to 10 MAGIC file  names.  
                   A MAGIC file name is a STATIC name someone can  use  
                   when  they do a file request and always be  assured  
                   of getting the current file.

                   For  instances,  the name of  the  current  Fidonet  
                   nodelist  changes each week. If you want to set  it  
                   up  so that all a person has to do is file  request  
                   NODELIST  and  get the current  nodelist  then  you  
                   would set up a MAGIC name:

                   NODELIST NODELIST.A57

                   NODELIST.A57  would  be THIS weeks  nodelist,  next  
                   week you'd have to do something like

                   NODELIST NODELIST.A64

                   Phoenix  will  search  the  directories  listed  in  
                   REQUEST.CTL for the NEW file name.

                   Examples:

                   NODELIST NODELIST.A57
                   OSIRIS SE401?.ARJ
                   ISIS I6*.ARJ

                   To  define a magic name, move the mouse  cursor  to  
                   one of the boxes in the column labeled "MAGIC NAME"  
                   and  click the LEFT mouse button then TYPE  in  the  
                   MAGIC name, e.g. OSIRIS.

                   TO define the NEW name for the MAGIC name you  just  
                   entered, move the mouse cursor to the corresponding  
                   box  in the column labeled NEW NAME and  click  the  
                   left mouse button.

                                      Summary

              AFTER  you have filled out the fields on screens,  click  
              on the EXIT BOX. 

              If  you have LEFT any REQUIRED fields EMPTY,  CONFIG.EXE  
              will  not allow you to SAVE or QUIT until  those  fields  
              have been filled in.

              The  remaining  options  COM IRQS, and  EVENTS  will  be  
              covered later.




         Phoenix           Technical Reference Manual        Page  19

                               Nodelist.dat And Domain.idx

                   This  is your PRIMARY nodelist, DOMAIN.IDX  is  the  
                   index, and you have TWO ways of creating it.

                                           Ned

                        The FIRST and easiest method is to simply  run  
                        NED.EXE.  It  will create  NODELIST.DAT  along  
                        with the DOMAIN.IDX. 

                        NED   will   also   create   SYSNAME.IDX   and  
                        BBSNAME.IDX These are optional INDEX files and  
                        we'll explain what those files are in the next  
                        section.

                        Use this approach if you are using Phoenix  in  
                        a  business environment or in  an  environment  
                        that doesn't provide a NODELIST.XXX text file.

                                            Makenl

                        Creating Nodelist.dat and Domain.idx with NED  
                        is  easy and painless, but it isn't  a  viable  
                        method  if you belong to a large network  like  
                        Fidonet. Fidonet has a new nodelist that comes  
                        out  weekly  and  contains  more  than  16,000  
                        systems.  Adding  those by hand, well  by  the  
                        time  you got them added you'd have  to  start  
                        over again with the new nodelist.

                        MAKENL  takes  the raw nodelist.xxx  file  and  
                        compiles  it into a Phoenix nodelist  complete  
                        with  HASH tables for Sysops name,  BBS  name,  
                        and finally DOMAIN address.

                                            Network Nodelist

                                  To   compile  a   NETWORK   nodelist  
                                  (Fidonet, TCP/PC, Family Net, etc. )  
                                  you  call  MAKENL with  the  command  
                                  line

                                  /N<NAME OF NODELIST>

                                  E.g. MAKENL /NNODELIST.157

                                  This,  in the case of  Fidonet,  CAN  
                                  generate a rather large NODELIST.DAT  
                                  file.  The size of the  NODELIST.DAT  
                                  file  for Fidonet's NODELIST.157  is  
                                  about 1.8 Meg.


         Phoenix           Technical Reference Manual        Page  20

                                  But,  you do have options  that  can  
                                  reduce  the size without having  any  
                                  impact on your ability to do mail.

                                  Since  Phoenix  is based  on  TCP/PC  
                                  routing   and  Fidonet  supports   a  
                                  similar, although a somewhat limited  
                                  version  of it, you do NOT  have  to  
                                  have  a  nodelist record  for  every  
                                  system.

                                  The  section  on ROUTING  goes  into  
                                  details  on how this works, but  for  
                                  now   just  assume  that  what   I'm  
                                  telling you is factual.

                                  You  can  reduce  the  size  of  the  
                                  nodelist.dat  file by  reducing  its  
                                  depth.

                                  Lets  assume your zone is 1. If  you  
                                  rarely  do mail with anyone  outside  
                                  your ZONE, then you can let the ZONE  
                                  GATE handle routing any messages you  
                                  may send. If you do mail with only a  
                                  couple of systems outside your ZONE,   
                                  you can include a PERSONAL  nodelist  
                                  with for those systems.

                                  If  you  want to do  that,  you  can  
                                  reduce  the  nodelist.dat  file   by  
                                  about 800K by including the  command  
                                  line switch /Z1

                                  This  means,  only keep  systems  in  
                                  ZONE 1. Ignore the rest.

                                  This  will  have no impact  on  your  
                                  ability to send mail except you will  
                                  HAVE to route mail to those  outside  
                                  your ZONE  to the  ZONEGATE.  

                                  You  can further reduce  the  depth,  
                                  and   size,  of  your  nodelist   by  
                                  including /R on the command line.

                                  /R   means   generate   a    routing  
                                  nodelist. 






         Phoenix           Technical Reference Manual        Page  21

                                  It  is kind of hard to explain  what  
                                  this means, but here goes.

                                  Only specific systems are  retained,  
                                  those need for routing purposes.

                                  For  instances, 1.247.0.0  would  be  
                                  retained while 1.247.456.0 would  be  
                                  ignored.  Ignored because you  could  
                                  route   1.247.456.0's  messages   to  
                                  1.247.0.0  and he could route it  to  
                                  1.247.456.0 for you. 

                                  This isn't something you have to  do  
                                  manually, Phoenix knows how to do it  
                                  and can do it automatically  without  
                                  your help.

                                  If  you were to compile the  Fidonet  
                                  nodelist.157  (16000+  systems  were  
                                  listed) using the command line:

                                  MAKENL /NNODELIST.157 /R /Z1

                                  You  would  produce  a  NODELIST.DAT  
                                  file  only 37K in size and, this  is  
                                  important,  you could STILL do  mail  
                                  with   every   system   listed    in  
                                  NODELIST.157. Most would be  routed,  
                                  a few could go direct.

                                  Due to limited routing  capabilities  
                                  in Fidonet, you will not be able  to  
                                  send  mail to SOME  systems,  mostly  
                                  POINTS.  You can get around that  by  
                                  using the Nodelist editor and ADDING  
                                  those  systems to your  nodelist  or  
                                  you can create a CUSTOM nodelist for  
                                  those systems and merge it with your  
                                  existing nodelist.dat file.
         
                                  If you use /R and you have to  route  
                                  mail  to those under you,  you  will  
                                  need  to  make  a  PRIVATE  nodelist  
                                  listing  the  individual  NODES  and  
                                  merge    it   with    the    exiting  
                                  NODELIST.DAT file. 







         Phoenix           Technical Reference Manual        Page  22

                                      Merging Multiple Nodelists

                                  If  you  plan  on  MERGING  multiple  
                                  nodelists, you have two methods. 

                                  The  EASIEST and quickest method  is  
                                  to use the dos copy command.

                                  Let's   assume  you  are  going   to  
                                  compile two nodelists,  nodelist.167  
                                  and worldnet.200.

                            Copy nodelist.167+worldnet.200  nodelist.doc
                            Makenl /Nnodelist.doc


                                  Dos would combine the two  nodelists  
                                  into a single file, nodelist.doc.

                                  You then compile nodelist.doc.

                                  The second method isn't as fast  and  
                                  requires  that you make  two  passes  
                                  with -M and one with -H.

                                  -M  lets MAKENL know that it  should  
                                  NOT     overwrite    the     exiting  
                                  nodelist.dat file (you should delete  
                                  your  old nodelist.dat  file  before  
                                  starting  the process of building  a  
                                  BRAND new one). It also tells MAKENL  
                                  not  to mess with building the  HASH  
                                  tables.

                                  MAKENL -NNODELIST.157 -M -Z1
                                  MAKENL -NFAMNET.166 -M
                                  MAKENL -H

                                  You  do not have to include  -T,  -M  
                                  automatically   turns   BUILD   HASH  
                                  TABLES off.


                                  -H tells MAKENL to rebuild the  HAST  
                                  tables.

                                  While  either  method will  work,  I  
                                  recommend   using   the   DOS   copy  
                                  command.





         Phoenix           Technical Reference Manual        Page  23

                                     Personal Or Private Nodelist

                                  You  may  want  to  include   system  
                                  records  in your NODELIST for  those  
                                  systems  not listed in your  NETWORK  
                                  nodelist. 

                                  You   might  do  this  for   points,  
                                  NODE under you if you are a NET host  
                                  and you use the /R command, or for a  
                                  few  select systems in  other  ZONES  
                                  when you use the /Zxx switch.

                                  To  create and maintain  a  personal  
                                  nodelist,     use    the     program  
                                  PRIVATE.EXE.

                                  Private is pretty simple to use  and  
                                  it isn't very fancy. You may use  it  
                                  once in a blue moon so we didn't  go  
                                  overboard trying to impress you with  
                                  out programming skills.

                                  You run the program with one of four  
                                  command line switches; /A, /L, /Exx,  
                                  and /Dxx.

                                  /A - Add a NEW record.
                                  /L - Generate PRIVATE.TXT. This is
                                  a text list of the private records.

                                  /Dxx - Delete Record xx. xx would be  
                                  the   RECORD   number   listed    in  
                                  PRIVATE.TXT.

                                  /Exx  - Edit Record xx. xx would  be  
                                  the   RECORD   number   listed    in  
                                  PRIVATE.TXT.

                                  Private.exe   keeps   the   personal  
                                  nodelist  records in a  file  called  
                                  PRIVATE.DAT. 

                                  When  you  run  MAKENL  with  /N  to   
                                  generates a nodelist from a  NETWORK  
                                  list,  the records from  PRIVATE.DAT  
                                  will automatically be included.







         Phoenix           Technical Reference Manual        Page  24

                                         Including Static Data

                                  When  you have Systems  with  static  
                                  data:   Session   Level   Passwords,  
                                  Session   TYPE,  OK  to   Drop   off  
                                  Echomail,   or   PREDIAL    strings,  
                                  creating  a  NEW  nodelist.dat  file  
                                  from a NETWORK list would  overwrite  
                                  that information.

                                  It would be a PAIN to have to  edit,  
                                  with   the  nodelist   editor,   the  
                                  information back in by hand.

                                  You  can  have  MAKENL  update   the  
                                  NODELIST  records  to  include   the  
                                  STATIC data for you. 

                                  You first create a STATIC   database  
                                  using  the program  STATIC.EXE.  

                                  It     functions    exactly     like  
                                  PRIVATE.EXE   only  with   different  
                                  database  fields. It has  the  exact  
                                  same command line switches.

                                  When you run MAKENL with the command  
                                  line  /N, MAKENL will  automatically  
                                  update the nodelist records with the  
                                  information  found  in  the   STATIC  
                                  DATABASE.  

                                              Hash Tables

                                  Phoenix  uses  several  compact  and  
                                  very  fast  HASH tables  to  find  a  
                                  system's  nodelist  record.   MAKENL  
                                  will create 4 different HASH Tables:

                                  DOMAIN.IDX,  contains the hash  code  
                                  for ZONE, NET, NODE, and POINT. 

                                  SYSNAME.IDX  contains the hash  code  
                                  for the SYSOPS name.

                                  BBSNAME.IDX  contains the hash  code  
                                  for the Name of the Mailer/BBS.

                                  PASSWORD.DAT contains the hash  code  
                                  for systems that have password.

                                  The  tables  are  compact.  If   you  
                                  created  a  HASH  table  for  16,500  
                                  systems, the size of the  DOMAIN.IDX  
                                  would be 100K. In fact the size  for  
                                  the  SYSNAME,   and  BBSNAME  tables  
                                  would also be 100K (individually).

                                  If you had 16,500 systems listed  in  
                                  the  nodelist.dat  file,  you  would  
                                  have four, 100K, Hash Tables with  a  
                                  combined size of 300K.

                                  You  do NOT have to keep ALL of  the  
                                  Hash Tables.

                                  For   instances,  only  the   matrix  
                                  editor uses the SYSNAME and  BBSNAME  
                                  tables  so  you can enter  just  the  
                                  sysops  name or the name of the  BBS  
                                  when  you  enter a message.  If  you  
                                  don't  need  that,  you  can  delete  
                                  them.

                                  DOMAIN.IDX  is the ONLY  Hash  Table  
                                  you  HAVE to keep. If you don't  you  
                                  can't do mail with anyone. In  fact,  
                                  Phoenix  will exit with an error  if  
                                  DOMAIN.IDX does not exist.

                                              Other Files

                                  MAKENL  might create one  additional  
                                  file  and  you  HAVE  to  keep   it,  
                                  PREDIAL.DAT.      This      contains  
                                  information   about   the    PREDIAL  
                                  strings and which system has one. 


                                        Phone.ctl

                   This    brings  us  to  our  final  REQUIRED  file,  
                   Phone.ctl,  the  phone number  translation  control  
                   file.   This  is used to translate  phone   numbers  
                   into a form that can be dialed from your location.

                   Phone.ctl  contains  two fields per line,  WHAT  TO  
                   LOOK FOR and WHAT TO REPLACE IT WITH.

                   E.g.
 
                   1314335 335                         
                   1314334 334 

                   The  first  field contains the numbers to look  for   
                   and    if   they're found, replace  those   numbers   
                   with  the  contents of the second field. 


         Phoenix           Technical Reference Manual        Page  25

                   You  should  ALWAYS place smaller  numbers  at  the  
                   bottom of  the file. 

                   1314335 335 
                   1314334 334 
                   1314 1 
                   1814 1 

                   Line 1 and 2 translates local phone numbers. Line 3  
                   and 4 translates same-area-code to just a 1. 

                   Let's  assume   the original  phone   number    was  
                   13143346359. 

                   Line 1 is ignored, 1314334 does not match 1314335. 
 
                   It would be translated to 3346359 by line 2. 

                                      Summary

              This  concludes the basic installation process  and  you  
              should  be ready to put Phoenix on-line. But before  you  
              do, read the section labeled "TEST DRIVE".

                             Phoenix Command Keys

         While  PULL down menus, exploding windows, and  snappy  sound  
         effects  are  nice,  we decided the extra  code  required  to  
         product  the  pull down menus, exploding windows,  and  sound  
         effects would not enhance the usability of this application.

         Since  a mailer generally runs unattended, we decided  to  go  
         with  the  faster HOTKEY approach with  simpler  and  cleaner  
         display  screens.  When  you DO need  to  interact  with  the  
         application, you don't want to have to wade though a bunch of  
         flashy windows and menus to get anything done.

         The command keys are broken into three LOGICAL segments,  ALT  
         keys, REGULAR keys, and CTRL keys.

         ALT  keys  and REGULAR keys reference Phoenix  functions  and  
         CTRL  keys reference Osiris related functions. If  you  don't  
         have Osiris, the CTRL keys will not function.

                                Phoenix Related Keys

                   Esc,  Displays  the command key help menu.  If  you  
                   can't  remember what key does what, press ESC  then  
                   enter your selection.

                   Enter,  If  you don't think your  modem  is  acting  
                   right,  you  can force Phoenix to  CLEAR  and  then  
                   reinitialize the modem by pressing the ENTER key.

         Phoenix           Technical Reference Manual        Page  26

                   When  Phoenix  CLEARS the modem, it sends  the  +++  
                   command  sequence to force the modem  into  command  
                   mode. It then drops DTR and holds it low for  about  
                   1.5   seconds.   And   finally,   the   modem    is   
                   initialized.  With  the modem  already  in  COMMAND  
                   MODE, the initialization process isn't likely to be  
                   ignored for any reason.

                   ?,  Opens a small window on the  screen  displaying  
                   the NAME of the current EVENT and the starting time  
                   for the NEXT event.

                   B, Activates SCREEN BLANKER.

                   Alt-M, Packet control system. When you select  this  
                   option, you'll get a screen listing the packets,  a  
                   packet is an individual *.MSG, 15 packets per page.  
                   You  can  use  PgUp and PgDn to  move  through  the  
                   packets.

                   Each  line displays the packet number, who  it  was  
                   originally addressed to (Domain Address), who it is  
                   routed  to  (Domain Address), The  TYPE  of  packet  
                   (ECHO, MSG, FILE, REQ, SRV, or TIC), and the STATUS  
                   (HOLD, SEND, H/CRSH, or S/CRSH). H/CRSH is a  CRASH  
                   message on HOLD while S/CRSH is a CRASH message set  
                   to  SEND. If you use the KILL option while  in  the  
                   packet  control system, some packets may  have  the  
                   STATUS of 'DEL' to indicate a deleted packet.

                   Besides  PgUp  and  PgDn, you  have  several  other  
                   commands: 

                   [Q]uit takes you back to waiting for mail mode.

                   [S]end  toggles  the SEND status  of  a  particular  
                   message,  if it was SEND it goes to HOLD and if  it  
                   was HOLD it goes to SEND . 

                   This is a TEMPORARY change and the message  reverts  
                   to  its original status when you EXIT  the  mailer,  
                   the  event changes, you do a mail session,  or  you  
                   TOGGLE the SEND status.

                   When you press S, Phoenix will ASK you which packet  
                   to  toggle, enter the PACKET number  (displayed  in  
                   the first column).

                   [C]rash   toggles  the  SEND/CRASH  status   of   a  
                   particular message. If it was NOT a crash  message,  
                   it  becomes  one. If it WAS a  crash  message,  the  
                   crash flag is removed. This is a PHYSICAL change to  
                   the actual message.

         Phoenix           Technical Reference Manual        Page  27

                   When you press C, Phoenix will ASK you which packet  
                   to  toggle. Enter the PACKET number  (displayed  in  
                   the first column).

                   [K]ill  physically  DELETES the  message.  If  that  
                   message  had a file attach and the file attach  was  
                   marked KILL after sending, the file attach is  also  
                   DELETED.

                   When you press K, Phoenix will ASK you which packet  
                   to kill. Enter the PACKET number (displayed in  the  
                   first column).

                   You can mix KILL and CRASH but you may not intermix  
                   KILL  with  toggle SEND. When you  KILL  a  message  
                   Phoenix  will rescan the matrix area,   reload  the  
                   event,  and redo any EXPLICIT routing  instructions  
                   when you exit the packet control system. If you had  
                   TOGGLE SEND, it would be undone.

                   [R]oute,  lets you alter the  destination  address.  
                   This is a TEMPORARY change and does NOT  physically  
                   alter  the message. The address will revert to  its  
                   original  destination  address  when you  EXIT  the  
                   mailer,  the  event  changes,  or  you  do  a  mail  
                   session.

                   [N]ext,   lets  you  alter  the  normal  dial   out  
                   sequence.  If  you want 1.100.10.0 to be  the  next  
                   system  dialed, press N and then enter  the  PACKET  
                   number.  

                   Alt-E, Load Phoenix Matrix Editor.

                   Alt-T,  Clears the TIMES CALLED counters.  This  is  
                   the  counter used to track the number of times  you  
                   call a specific system during an event.

                   Alt-B, Clears the BUSY signal counters. This is the  
                   counter that tracks the number of BUSY signals  you  
                   get  when  you  call a specific  system  during  an  
                   event.

                   Alt-N, Load the NODELIST editor.

                   Alt-R,  Reload Msgs, reload event information,  and  
                   reload any EXPLICIT routing instructions.

                   Alt-D,  Shell  to  DOS.  Type  EXIT  to  return  to  
                   Phoenix.

                   Alt-F, Displays the F-KEY definition tables. 


         Phoenix           Technical Reference Manual        Page  28

                   Alt-P, Poll a specific system. Phoenix will ask you  
                   for  the  FULL Domain Address. Keep  in  mind  that  
                   Phoenix  uses a PERIOD to separate the  subdomains.  
                   If  the domain address matches one of  the  systems  
                   listed  in  the nodelist, Phoenix will  generate  a  
                   CRASH/DIRECT poll packet.

                   Alt-C,  Configuration System. Any changes you  make  
                   in  your  primary  or any subsystem  will  go  into  
                   effect ASAP.

                   Alt-H,  HISTORY system. This displays  the  current  
                   call  history. Press any key to return  to  waiting  
                   for  call  mode. If you want to CLEAR  the  History  
                   database, press ESC.

                   Alt-G,  This accesses the GRAPHICS History  screen.  
                   If  you  do not have VGA, this  function  will  not  
                   work.  You should have the program PAC.EXE  in  the  
                   Phoenix  directory  or in a PATHED  directory.  PAC  
                   contains  the  code required to generate  the  high  
                   resolution graphics screens.

                   Alt-W,  shows WHO you last did mail with and  when.  
                   Phoenix  will  track  the  last  100  to  110  mail  
                   sessions.   When  you  reach  111,   Phoenix   will  
                   automatically trim it back to 100.

                   When  the Display page is full, Phoenix  will  BEEP  
                   and wait for you to press ENTER for the next  page,  
                   press ESC to abort. You'll also notice a black  bar  
                   on  the  screen. This is a VISUAL aid and  you  can  
                   move the bar with the up and down arrow keys.

                   Alt-S, Lets you SEND a FILE ATTACH or FILE  REQUEST  
                   to  another  system  without  entering  the  matrix  
                   editor. The system MUST be in your nodelist.

                   Alt-A, enter TERMINAL mode. 

                              Osiris Related Functions

              The  OSIRIS related functions will ONLY be available  if  
              you  are  running Osiris. If you aren't, they  will  not  
              show up on the help menu (they will, but they will be in  
              a color that is very hard to see).

              Ctrl-O, Run OSM.
              Ctrl-T, Run CAT.
              Ctrl-E, Run Sysop Editor (Sphinx).
              Ctrl-L, Local Log-on.



         Phoenix           Technical Reference Manual        Page  29

              Ctrl-S,  BBS  Statistics. This shows last  caller,  when  
              they   called,   number  of  calls  today,   number   of  
              uploads/downloads  for today, TOTAL calls to  the  node,  
              and  it  will also tell you if the sysop  has  any  mail  
              waiting. This functions on nodes 1 - 8.

              Phoenix will switch you to the OSIRIS= directory  before  
              calling any of the OSIRIS related programs. 

                      Routing Principles And Architecture

         When  you have a LARGE number of systems, it isn't  practical  
         to  keep  a  nodelist  record of  every  system  for  several  
         reasons.  You don't do mail with every system in the  network  
         and it can take a lot of disk space. 

         There  are two methods we can use to get around the  problem:  
         Use  an addressing system that doesn't require a nodelist  or  
         develop an IMPLIED routing system.

         Routing: to direct, send, forward mail along a specific  PATH  
         to its final destination.

         HTMS  uses  the  PHONE NUMBER as  the  address.  This  method  
         doesn't need a nodelist and doesn't require another  system's  
         cooperation.  The drawback to HTMS:  When you in a  situation  
         where you NEED to route, it is hard to do (from a programmers  
         point of view) and in some cases, impossible.

         An extensive ROUTING system is the other method of doing  the  
         same thing. While this method does allow you to do away  with  
         large nodelists, it does have several drawbacks. It can  take  
         a  little longer, a day or so, to get a message from point  A  
         to point B and it does require other systems cooperation.

                                  Types Of Routing

              There are TWO types of routing, IMPLIED and EXPLICIT.
                                     Implied Routing

                   Implied routing is what Phoenix does INTERNALLY and  
                   in absents of any EXPLICIT routing instructions.

                   In  other words, without giving precise  and  clear  
                   instructions  on  HOW to send a  message,  you  are  
                   implying  that Phoenix should use four  dimensional  
                   network  routing  to get the message to  its  final  
                   destination.






         Phoenix           Technical Reference Manual        Page  30

                                    Explicit Routing

                   Explicit routing is just that. You are giving CLEAR  
                   and  precise  instructions  on  how  to  send   the  
                   message.

                   You  might  have used the DIRECT flag.  The  DIRECT  
                   flag is an EXPLICIT routing instructions.

                   You  might have used a special ROUTE  control  file  
                   during  the  event.  A  ROUTE  control  file  gives  
                   EXPLICIT routing instructions.

              Throughout this document, when we say simply ROUTING, we  
              are referring to IMPLIED ROUTING.

                             How Implied Routing Works

              Assuming  that  a Network has the ZONE of 1.  It  has  2  
              different  NETs, 1 and 2. Each NET has 2 NODES and  each  
              NODE has 2 POINTS.

              1.0.0.0 <- Zone Level System.
              1.1.0.0 <- NET 1
              1.2.0.0 <- NET 2
              1.1.1.0 <- NET 1, NODE 1.
              1.1.2.0 <- NET 1, NODE 2.
              1.2.1.0 <- NET 2, NODE 1.
              1.2.2.0 <- NET 2, NODE 2.
              1.1.1.1 <- NET 1, NODE 1, POINT 1.
              1.1.2.2 <- NET 1, NODE 2, POINT 2.
              1.2.1.1 <- NET 2, NODE 1, POINT 1.
              1.2.2.2 <- NET 2, NODE 2, POINT 2.

              This  Network contains a total of 11  systems.  However,  
              the maximum number of REQUIRED nodelist records for  any  
              system in the network is 2 and in several cases 1.  Yet,  
              every  system in the network can communicate with  every  
              other system.

              When  1.2.2.2  sends mail to 1.1.1.1, it  is  routed  to  
              1.2.2.0.  The  message  will continue  to  traverse  the  
              network until it arrives at its final destination.

              It  traverses  the  network  in the  one  of  two  ways,  
              depending  on  the depth of the nodelists used  by  each  
              system.

              Method #1

              1.2.2.2  -> 1.2.2.0 -> 1.2.0.0 -> 1.0.0.0 -> 1.1.0.0  ->  
              1.1.1.0 -> 1.1.1.1


         Phoenix           Technical Reference Manual        Page  31

              Method #2

              1.2.2.2 -> 1.2.2.0 -> 1.2.0.0. -> 1.1.0.0 -> 1.1.1.0  ->  
              1.1.1.1

              When  a  message  is routed  from  1.2.0.0  directly  to  
              1.1.0.0,  it  is referred to as   cross  level  routing.  
              Cross level because 1.2.0.0 and 1.1.0.0 are both on  the  
              same level, NET systems.

              Figuring  out before hand HOW a message will  be  routed  
              isn't  difficult, as long as you only have  one  address  
              within  that network. Routing is based on YOUR level  in  
              the network. 

              If you are a POINT, a POINT can be identified by a  NONE  
              ZERO  POINT subdomain, messages are always routed UP  to  
              the NODE above you. 

              It  is  POSSIBLE  that the NODE  may  QUIT  the  network  
              leaving  your without a NODE. If that  happens,  Phoenix  
              will BYPASS the NODE and go directly for the NET  system  
              above  you.  If by some weird chance of  fate,  the  NET  
              system has also quit, Phoenix would attempt to route  to  
              the ZONE (he will always be there).

              If you are a NODE, a NODE system can be identified by  a  
              NONE  ZERO  NODE subdomain and a ZERO  POINT  subdomain,  
              messages are either routed UP or DOWN. UP to the NET  or  
              DOWN  to  the  POINT  level. If the  NET  above  you  is  
              missing, quits the network, Phoenix will bypass the  NET  
              and go directly to the ZONE.

              If  you  are  on  the NET level, a  NET  system  can  be  
              identified  because  he  has ZERO NODE  and  ZERO  POINT  
              subdomains, message are either routed UP, DOWN, or CROSS  
              LEVEL. UP to the ZONE, DOWN to the NODE, or CROSS  LEVEL  
              to another NET.

              If  you  are a ZONE system, IMPLIED  routing  is  always  
              DOWN, to the NET system. 

                           Common Questions Concerning Routing

                   Q:  I'm 1.235.400.0 and I'm suppose to  route  mail  
                   for those in my net (235).

                   A:  No, you aren't and can't route mail for  others  
                   in and OUT of your NET. 

                   At least you are not going to do that with  IMPLIED  
                   routing.


         Phoenix           Technical Reference Manual        Page  32

                   Q: Why?  

                   Because  you're  a NODE and a NODE can  only  route  
                   mail UP and DOWN. 

                   In  order  to automatically route mail,  you  would  
                   also have to have a NET address.

                   If  you  were 1.235.400.0  AND  1.235.0.0,  Phoenix  
                   could automatically route the mail.  


                   Q: Suppose someone sends a message to my system for  
                   1.237.500.5 and I'm 1.235.400.0

                   A:  Implied routing will route it to 1.237.0.0,  he  
                   is  YOUR  NET  host.  It  will  NOT  route  it   to  
                   1.237.500.0, that is the NET hosts job and you  are  
                   not a NET host. 

                   Q: It doesn't work that way in Fidonet!

                   A:  Yes  it does, however . . . Fidonet  is  a  two  
                   dimensional network and routing, although  similar,  
                   is a little different. And, most of the mailers you  
                   find that were orginally written for Fidonet  only,  
                   have very limited routing capablities. 

                   Q: Can I override Implied Routing?

                   A:  Yes you can. You can either turn it off or  use  
                   EXPLICIT  routing instructions to force mail to  be  
                   routed in a specific manner.

                   Q: What if I belong to multiple networks?

                   A:  Phoenix  can automatically route  mail  without  
                   instructions  from you, 99.9 percent of  the  time,  
                   even  if  you define 54 addresses in  54  different  
                   networks  or  54 different addresses  in  the  same  
                   network.

                   Q: How is that Possible?

                   A: Phoenix has an A.I. routing system. A simplified  
                   explaination; It finds the highest address you have  
                   defined  within  a  specific  zone  and  within   a  
                   specific  net and uses that address to  figure  out  
                   routing. 

                   If you do not have an address for that NET, it uses  
                   the highest address defined for the zone.


         Phoenix           Technical Reference Manual        Page  33

                                 What About Crash?

              CRASH means send ASAP but do it according to the  DIRECT  
              flag.

              It is likely that you want your mail routed, you are  at  
              the  POINT level, but you want your mail to get  to  the  
              NODE level ASAP. That is where CRASH comes into play.

              The Routing architecture I've outlined above is built-in  
              and done without any special instructions on your  part.  
              You don't have to setup any type of route control  files  
              or even WORRY about how it all works.

                              Implied Routing Limited

              When  you set IMPLIED ROUTING to "LIMITED",  CONFIG.EXE,  
              IMPLIED  routing  works  a  LITTLE  different.   LIMITED  
              routing  turns OFF routing for anything that has a  FILE  
              ATTACH.  This includes TIC, ECHOMAIL, SERVICE  REQUESTS,  
              FILE REQUESTS, and any other type of FILE. 

              This   does   NOT  preclude   using   EXPLICIT   Routing  
              instructions,  covered later. However, it does mean  you  
              can  only  send  FILES to  systems  that  HAVE  nodelist  
              records.

                              Implied Routing Disabled

              When you set IMPLIED ROUTING to "DISABLED",  CONFIG.EXE,  
              IMPLIED  routing  is all but disabled and no attempt  is  
              made  to route ANYTHING. It isn't TOTALLY  disabled,  it  
              will FREEZE any messages/files, etc. to UNKNOWN systems.

              This   does   NOT  preclude   using   EXPLICIT   Routing  
              instructions, covered later. However, it does mean every  
              system  you  communicate  with has to  have  a  nodelist  
              record. 
                                  Explicit Routing

              There  may  be  cases where you  need  EXPLICIT  Routing  
              instructions or NO routing at all.

              Phoenix lets you define a special EXPLICIT route control  
              file, totally optional, for each event (events are  also  
              optional).  You define the route control file  when  you  
              set up an event. See section on events for details.







         Phoenix           Technical Reference Manual        Page  34

              Each  EXPLICIT  route control file you create  uses  one  
              EXPLICIT  routing command per line, unlimited number  of  
              lines.

              Each  command acts independently  of the  last  command,  
              TOP DOWN processing.

              The following EXPLICIT ROUTE Nouns are available:

              FORWARD FOR
              NO ROUTE
              SEND TO
              ROUTE {} TO {}
              HOLD
              DIAL DELAY
              BUSY ATTEMPTS
              FORWARD FILE
              MAXIMUM CONNECTS
              POLL
              USE ADDRESS {} For {}
              ECHO PROCESSING {ON/OFF}
              GATE {} TO {}

              Each Noun is followed by ONE of the following verbs:

              Domain Address
              Wild-Domain Address
              FILES
              TIC
              CRASH
              ECHOMAIL

              A Domain address is a SPECIFIC 4 dimensional address.

              E.g. 1.242.200.0

              You  MUST  use  a  PERIOD  to  separate  the  individual  
              subdomains.

              A WILD-DOMAIN address is almost like the regular  domain  
              address but, you can use the DOS wildcard character  '*'  
              in place of any or all of the individual subdomains.
              
              And  like the DOS '*', '*' will match anything  in  that  
              position.

              E.g. 1.237.*.0

              Would match 1.237.1.0, 1.237.2.0, 1.237.45.0, etc.





         Phoenix           Technical Reference Manual        Page  35

              This  is used to address systems by GROUPS  rather  than  
              individually.

              Look closely at the TYPE of address the route noun uses.  
              You  can  use a straight domain address in  place  of  a  
              WILD-DOMAIN  address  but you CANNOT use  a  WILD-DOMAIN  
              address in place of a straight domain address.

              The WILD-DOMAIN address also supports the question mark.

              You  may  use the question mark in place of  any  single  
              digit within the NODE or POINT fields.

              E.g.  1.296.20?.0 or 1.296.?00.2?

              The QUESTION mark will match any digit. 


                            Forward For {Wild-Domain Address}

                   The  default  is forward for  anyone,  required  on  
                   certain  levels within TCP/PC, Fidonet,  and  other  
                   public domain packet networks.

                   However, if you are on the POINT level you are not  
                   required  to forward for anyone. If you are on  the  
                   NODE level and do not have any POINT systems  under  
                   you,  you can disable forwarding without  violating  
                   network regulations.

                   Example:

                   FORWARD FOR 1.237.504.4
                   FORWARD FOR 1.*.*.*
                   FORWARD FOR 1.237.504.*
                   FORWARD FOR 1.237.*.*

                   To DISABLE FORWARDING, use your OWN address.

                   If you are 1.237.504.0, using the statement

                   FORWARD FOR 1.237.504.0 

                                     No Route {Verb}

                   You  can override IMPLIED routing with the noun  NO  
                   ROUTE followed by a single verb. The verbs are:

                   {Wild-Domain  Address},  FILES,  CRASH,  TIC,   and  
                   ECHOMAIL.




         Phoenix           Technical Reference Manual        Page  36

                   TCP/PC  specifications DO provide for routing  file  
                   attaches.  However not all networks  allow  routing  
                   files  and/or  echomail  and some  mailers  do  not  
                   support file routing.

                   If  the network you belong to doesn't support  FILE  
                   routing, you have two options:

                   Include

                   NO ROUTE FILES
                   NO ROUTE TIC
                   NO ROUTE ECHOMAIL

                   in all of your events.

                   Or set the IMPLIED ROUTING to LIMITED.

                   Example:

                   NO ROUTE 1.235.*.*
                   NO ROUTE 1.200.10.0
                   NO ROUTE *.*.*.*

                   The   last   one  totally  disables   routing   for  
                   everybody.

                              Send To {Wild-Domain Address}

                   Phoenix defaults all messages, unless marked CRASH,  
                   to HOLD. In other words, you have to tell it  which  
                   systems it can call during an event.

                   Messages  marked CRASH are the only  exceptions  to  
                   this rule.

                   You  tell Phoenix to PLACE a call to  a  particular  
                   system  or  group  of  system  with  noun  SEND  TO  
                   followed by  a Wild-Domain address.

                   SEND TO 1.*.*.*
                   SEND TO 1.237.*.0
                   SEND TO 1.237.*.*
                   SEND TO 1.*.0.0










         Phoenix           Technical Reference Manual        Page  37

                     Route {Wild-Domain Address} To {Domain Address}

                   This noun lets you route mail to a specific network  
                   domain address other than the one it would NORMALLY  
                   go to.

                   NOTE: DIRECT mail cannot be rerouted.

                   Examples

                   ROUTE 1.238.0.0 To 1.237.504.0
                   Route 1.*.*.5 To 1.100.10.10
                   Route *.*.*.* To 1.200.0.0

                   Take note of the second address, the one  following  
                   the  word  'TO'. It is NOT a  wild-domain  address.  
                   This is a standard domain address. 

                                       Hold {Verb}

                   The noun HOLD is used in conjunction with  SEND TO.  
                   You  can use the following verbs with HOLD:  {Wild- 
                   Domain address}, FILES, TIC,  and ECHOMAIL.

                   Example

                   HOLD 1.237.504.0
                   HOLD 1.234.100.*
                   HOLD *.*.*.*
                   HOLD FILES
                   HOLD TIC
                   HOLD ECHOMAIL

                           Forward File {Wild-Domain Address}

                   Forwarding files in TCP/PC is optional but not  all  
                   mailers  support file forwarding. Some NETWORKS  do  
                   not support file forwarding.

                   The   default  in  Phoenix  is  to   support   file  
                   forwarding but this noun lets you tailor or disable  
                   file forwarding.

                   Example.

                   FORWARD FILE 1.237.*.*
                   FORWARD FILE 1.235.505.*
                   FORWARD FILE 1.237.504.10

                   To DISABLE file forwarding, use your OWN address.

                   E.g. If you are 1.100.10.0 then


         Phoenix           Technical Reference Manual        Page  38


                   FORWARD   FILE   1.100.10.0   will   disable   file  
                   forwarding.
                                  Dial Delay {Seconds}

                   While  this is not a ROUTING noun, it  does  affect  
                   the delivery of mail. You can override the  default  
                   time between dial attempts during a specific event.  
                   It  will revert to the default dial delay when  you  
                   change to the next event.

                                 Busy Attempts {Number}

                   Again,  this is not a ROUTING noun but does  affect  
                   the  delivery of mail. If you are going to  call  a  
                   system during the event that is KNOWN to be a  very  
                   busy system, you may want to override the number of  
                   busy  signals a certain system is allowed to  have.  


                                Maximum Connects {Number}

                   This  determines the maximum number of CONNECTS  to  
                   any  single  system  during  this  event.  A   mail  
                   transfer  does NOT actual have to take  place.  You  
                   ONLY have to establish the physical connection.

                   {number} can be any number between 1 and 255.

                                Echo Processing {On/Off}

                   E.g.    Echo Processing Off
                   E.g.    Echo Processing ON

                   This  overrides the phoenix  configuration  setting  
                   ECHOMAIL.BAT  YES/NO during the current event.  The  
                   default  setting will be restored when the  current  
                   event ends.

                   Q: What's it for ?

                   Assume  you are an echomail hub and you send to  10  
                   systems. During an event, you send to system 2  but  
                   half way through the transfer, carrier is lost.

                   You proceed to send to system 3 and after you send,  
                   system  3 has echomail for you to pickup. You  pick  
                   it up and import it (and export any mail going back  
                   out).

                   After  you send to 4,5,6,7,8,9, and 10,  you  cycle  
                   back to system 2 (the one you lost carrier with 1/2  
                   through the transfer).

         Phoenix           Technical Reference Manual        Page  39

                   System 2 already has 1/2 of the file BUT . . .  you  
                   have ADDED to that file and the file's date  stamp,  
                   time  stamp, and file size has changed. That  makes  
                   it impossible for system 2 to resume the  transfer.  
                   He  will either ask for a SKIP or start a  NEW  DUP  
                   file. If he uses a DUP filename, his echo processor  
                   will not be able to process the bundle and the  OLD  
                   partial  bundle  will set there until  he  manually  
                   deletes it.

                   By  toggling  ECHO  PROCESSING OFF  during  a  SEND  
                   event, you have done way with this problem. Not  to  
                   mention spending what might amount to a LOT of time  
                   processing  echomail  when you really  want  to  be  
                   sending out what you already have.

                   "AND . . ."

                   Assume you are an echo hub for 20 systems. You have  
                   set-up a 3 hour event so those systems can POLL you  
                   for  echomail. You  might not WANT to  process  any  
                   echomail  THEY drop off because it WILL  take  away  
                   from the ON-LINE time others will have to PICK-UP.

                   Better to WAIT until AFTER the event when  everyone  
                   has  gotten their mail before  processing  anything  
                   they dropped off.


                   Q: Why Echo Processing ON ?

                   You  might want to set the default echomail.bat  to  
                   NO and ONLY process inbound echomail during one  or  
                   two specific events.

                   Lets  say  you  have a REAL  busy  BBS  during  the  
                   day/night.  You  might  want  to  delay  processing  
                   inbound  echomail  until  3 or  4  o'clock  in  the  
                   morning so your callers will have more TIME to  get  
                   on-line.

                    Use Address {Domain Address} For {Domain Address}

                   This  lets  you switch to a specific  address  when  
                   calling a specific system  during THIS event.

                   E.g

                   Use Address 99.23.3.0 For 99.23.0.0





         Phoenix           Technical Reference Manual        Page  40

                                  Poll {Domain Address}

                   This  is the final NON-ROUTE noun. This  guarantees  
                   that  you will have a message that will  trigger  a  
                   call  to a specific system during this  event.

                   Domain  Address is the FULL domain address for  the  
                   system you want to call. E.g., 1.235.504.9

                   Phoenix handles the POLL command by looking to  see  
                   if  you have CONNECTED to that system  during  this  
                   event.  If you haven't, then it will  generate  the  
                   POLL.  If you have, POLL is ignored.  Phoenix  will  
                   flag  incoming Mailer calls as an OUTBOUND call  to  
                   that  system.  The  purpose  is  to  prevent   POLL  
                   requests. If that system calls to pickup/drop  off,  
                   you don't want/need to place the a call TO him.

                   POLL doesn't create a PHYSICAL message. There is  a  
                   flag  in the packet table, this  holds  information  
                   about your messages, specifically for POLL.

                   A  NULL PACKET is ONLY used when Phoenix builds the  
                   temporary  packet, prior to placing the  call,  and  
                   nothing was packed.

                            Gate {Zone} To {Domain Address}

                   This a very SPECIAL noun and should only be used by  
                   a gateway between two networks.

                   {ZONE} is the  of the "OTHER" network. 

                   {Domain Address} is the full domain address of  the  
                   system in the "OTHER NETWORK".

                   Assuming  your address is 99.0.0.0 which  makes  you  
                   the  TOP most system in TCP/PC network.  Since  you  
                   are the TOP system, you're required to GATE  matrix  
                   between  your network and Fidonet (You may, but  it  
                   isn't required, also GATE files).

                   The  Fidonet  systems Domain  Address  is  1.1.99.0  

                   The statement: GATE 1 To 1.1.99.0

                   Would  ROUTE  anything  and  EVERYTHING,  including  
                   direct, that has the ZONE of 1 to 1.1.99.0.






         Phoenix           Technical Reference Manual        Page  41

                        (Examples Assume ROUTE TYPE DEFAULT)

                                    Examples #1

              Lets  assume  that you are a POINT with  the  domain  of  
              1.237.504.2  and you do run a 24hr mailer. You  want  to  
              call  the NODE you are under, 1.237.504.0, once a  night  
              to pickup echomail and any matrix mail, or to drop off.

              Other  than that, your mailer is used to front  for  the  
              BBS.

              You'll need to set-up one special event to achieve this,  
              see  the section on events for details on how to  set-up  
              the event. 

              Lets also assume that you defined the route control file  
              for this event as CALLHOST.CTL.

              The  first  two lines, the ONLY two lines you  need,  in  
              callhost.ctl:

              POLL 1.237.504.0
              SEND TO 1.237.504.0 

              The first line will make sure that there is SOMETHING to  
              trigger  a  call to 1.237.504.0. The second  line  tells  
              Phoenix  to place a call to 1.237.504.0, if  mail  exits  
              for that system.

              If  you have an echomail bundle or outbound matrix  mail  
              going  to 1.237.504.0, you HAVE to have the 2nd line  or  
              Phoenix will not make the call.

                                    Example #2.

              Lets assume that you are 1.237.0.0 and you are going  to  
              be  routing mail to and from 1.237.x.x, since you are  a  
              NET host, this is a requirement.

              You'll want to do this late at night when the rates  are  
              low  so  you'll  need to set-up an  event  and  a  route  
              control  file  for  this event. Lets  assume  the  route  
              control file is called SENDEM.CTL.

              SEND TO 1.0.0.0
              SEND TO 1.*.*.0
              HOLD 1.237.*.*
              POLL 1.0.0.0





         Phoenix           Technical Reference Manual        Page  42

                                     Example #3

              Lets assume you're address is 1.237.0.0 and you want  to  
              send  out  all  matrix mail  to  1.237.x.x,  EXCEPT  for  
              1.237.500.0, and you do NOT want to send Echomail or TIC  
              files. Those you want held for pickup.

              SEND TO 1.237.*.*
              HOLD 1.237.500.0
              HOLD TIC
              HOLD ECHOMAIL

              Notice  how the TOP DOWN command structure works?   

              Ok, but what if you want the TIC files for ONE  specific  
              system, 1.237.555.0, to GO.

              SEND TO 1.237.*.*
              HOLD 1.237.500.0
              HOLD TIC
              SEND TO 1.237.555.0
              HOLD ECHOMAIL

              You can make your customized routing files as simple  as  
              the  first  example, or as complex (or worse .  .  .MUCH  
              worse) as the last example.

                                 Common Mistake #1

              ROUTE 1.237.504.0 To 1.100.10.5
              HOLD 1.237.504.0

              If your intention was to HOLD the mail for  1.237.504.0,  
              it  would not work. The first line routed  1.237.504.0's  
              mail  to 1.100.10.5 and there would not BE any mail  for  
              1.237.504.0
                                 Common Mistake #2

              HOLD 1.237.504.0
              SEND TO 1.237.*.*

              In this example, above, you are sending mail to everyone  
              that  has  the address of 1.237.x.x but  1.237.504.0  is  
              down (hard drive blew up) and his mail is suppose to  be  
              held. 

              The  first line is executed and 1.237.504.0's  mail  was  
              placed  on  HOLD. However, you  countermanded  the  HOLD  
              command  with the SEND TO 1.237.*.* command. Since  SEND  
              TO  1.237.*.* was the last command executed, it  is  the  
              one that is retained.



         Phoenix           Technical Reference Manual        Page  43

                                   Tips On Speed

              There are TWO things you can do that will greatly reduce  
              processing time. 

              While  Phoenix is exceptionally fast, the IMPLIED  route  
              manager  actual does an enormous amount of work when  it  
              scans the matrix area. 

              Not only does it load the messages, but it calculates  a  
              number  of possible ROUTING paths to get the message  to  
              it's final destination.

              To  do this, it must repeatedly access the  nodelist  to  
              find  out if certain systems are or are not  listed  and  
              this is the most time consuming part.

              To  speed-up  this  process,   run  a  disk  cache.   If  
              possible, use at least a 128K cache.

              With  a 128K disk cache in place, Phoenix can  scan  the  
              nodelist  at the rate of 45,000 records per  second  (16  
              Mzh  386  with  a 25 Mls Hard  drive.  Faster  computers  
              and/or faster hard drives will product better speeds.

              Without a disk cache, same hardware, Phoenix could  only  
              scan at the rate of about 19,000 records per second.

              The  second  thing  you can do: DON'T  KEEP  THE  ENTIRE  
              NETWORK NODELIST.

              You  simply  do NOT need it. Even if you are a  NC  (Net  
              Coordinator) you only need the other NC's and the  NODES  
              in  your net. Along with maybe a few select systems  you  
              do  mail with on a regular bases. 

              Compile the fidonet nodelist with the /R switch and  use  
              a personal nodelist control file for the NODES under you  
              and those you do mail with regularly and let PHOENIX  do  
              its  job.  After  all, isn't that way  you  purchased  a  
              computer for in the first place? 

              Not only will this save you a great deal of disk  space,  
              but  the  overhead processing time will  be  drastically  
              reduced.

                                    Events
         
         An  EVENT tells Phoenix to ACT differently during a  specific  
         time frame.

         Events are OPTIONAL. If there is no ACTIVE event Phoenix uses  
         the following DEFAULTS:

         Phoenix           Technical Reference Manual        Page  44


         All mail, except CRASH, is placed on HOLD.

         Humans ARE allowed access to the BBS.

         BUSY and CONNECT restrictions are disabled.

         No  restrictions  on Number of files that  can  be  requested  
         during a single session.

         Time to Next Event is the starting time of the NEXT  event or  
         midnight if you have NO events defined.

         To define an event, run CONFIG.EXE and move your mouse cursor  
         to the BOX labeled "EVENTS" and click the LEFT mouse button.


                                 Event Lable

              This  is not used by Phoenix, it is display  so   you'll  
              know WHICH event is running. Phoenix has its own  method  
              of identifying events.
              
              The LABEL can be any name you want to call the event,  a  
              maximum  of 8 characters. The label doesn't HAVE  to  be  
              unique,  but I would recommend that you use a  different  
              name for each event.

                                   Starting Time

              This  tells  Phoenix  what time of  day  this  event  is  
              suppose to START.

              STARTING  TIME is in HH:MM format, military time.  Legal  
              starting times range from 00:00 to 23:59.

                                    Ending Time

              This tells Phoenix WHEN the event is suppose to END.

              ENDING  TIME  is in HH:MM format, military  time.  Legal  
              ending times range from 00:01 to 24:00.

              NO event may span midnight.










         Phoenix           Technical Reference Manual        Page  45

                                     Execute On

              This tells Phoenix which DAYS the event is suppose to be  
              active.

              To  ACTIVATE  the event for a particular day,  move  the  
              mouse cursor to the BOX under the DAY and click the LEFT  
              mouse button.

              If the event is ACTIVE on a particular day and you  want  
              to  DEACTIVATE  the event for that day  move  the  mouse  
              cursor to the BOX under the DAY and click the LEFT mouse  
              button.

              You  can  have  the  event  active  on  ALL  days,   any  
              combination  of  days or NONE. NONE is considered  as  a  
              PLACE holder.

                                      Dynamic

              This  means the event is ONLY suppose to be active  *IF*  
              there  is outbound mail. If there is NO  outbound  mail,  
              Phoenix terminates the event, even if it has not reached  
              the ENDING TIME.

                                        Warnings

                   If  you define an event as dynamic, do  not  define  
                   another  event that SENDS mail or POLLS  until  the  
                   ENDING  time  of  the  current  dynamic  event  has  
                   passed.

                   If the STARTING and ENDING time of a dynamic  event  
                   is  00:00  and 01:00, the next SEND or  POLL  event  
                   should NOT begin until AFTER 01:00.
                   
                   The  TIMES  CALLED, BUSY, and  POLL  databases  are  
                   reset  when Phoenix starts to place a call  or  the  
                   event  label  POLL is used and  the  CURRENT  event  
                   doesn't  match the event tag in the  TIMES  CALLED,  
                   POLL, and BUSY databases. 

                   This  is  what can happen if you  don't  listen  to  
                   this warning:

                   EVENT  PICKUPMAIL  is dynamic, runs from  00:00  to  
                   01:00 and has an event label POLL 1.237.504.0

                   The next event is NOT dynamic and runs from 00:00 to  
                   2:00 and says SEND TO 1.100.10.0




         Phoenix           Technical Reference Manual        Page  46

                   The  dynamic event runs, it POLLS  1.237.504.0  and  
                   picks up echomail.

                   After  the  mail is processed,  Phoenix  loads  the  
                   current  event,  PICKUPMAIL. Since  you've  already  
                   CALLED 1.237.504.0, POLL is ignored.

                   There  is  nothing  to SEND so  the  dynamic  event  
                   terminates and the next event starts.

                   You have echomail for 1.100.10.0 and you call. THAT  
                   CALL  RESETS the busy, connect, and poll  databases  
                   because that event tag doesn't match the one in the  
                   databases.

                   After you hang up, Phoenix loads the current event.  
                   Since  the  DYNAMIC  events  ENDING  time  has  NOT  
                   elapsed, it is STILL VALID. BUT when it checks  the  
                   POLL database it finds a different EVENT tag so  it  
                   CLEARS it and POLLS 1.237.504.0 

                   You  can  get  locked  into  a  cycle  of   POLLING  
                   1.237.504.0   to   pickup  echomail   and   CALLING  
                   1.100.10.0  to drop off the echomail you picked  up  
                   from 1.237.504.0.

                   This is the worse case scenario, it really  depends  
                   on what the next event is set to do. 

                   The best defense against anything like that, follow  
                   instructions.

                              Explicit Route Ctrl File

              This  is the name of a text file used to  hold  EXPLICIT  
              routing  instructions  for this event,  see  section  on  
              ROUTING for information on the contents of this file.

                                  Exit Errorlevel

              This  tells Phoenix to EXIT with a  specific  errorlevel  
              the first time it runs this event, it will only exit one  
              time per event. The errorlevel can be anything you  want  
              between  31 and 199. Phoenix reserves 1 - 30 and  200  -  
              255 for internal use.









         Phoenix           Technical Reference Manual        Page  47

                                    Event Batch

              This  is a simplified form of the "Exit Errorlevel"  but  
              without having to mess with errorlevels. The first  time  
              this event is executed, Phoenix will run the batch  file  
              you defined in this field. It will ONLY run the file one  
              time per event.

              You  can use "Exit Errorlevel" or "Event Batch" but  NOT  
              both.  In  fact, CONFIG will prevent you  from  defining  
              BOTH.  If you set an exit errorlevel, CONFIG will  CLEAR  
              the Event Batch field. If you select Event Batch, CONFIG  
              will change the Exit Errorlevel to 0.

                             Exit On Inbound Errorlevel

              This  tells Phoenix to exit with this  errorlevel  after  
              each INCOMING mail session.

              If  you've  used other mailers in the pass, you  may  be  
              tempted to use this to process echomail bundles that you  
              receive.  You do NOT have to use this label  to  process  
              inbound echomail.

              When   Phoenix   receives   an   ECHOMAIL   bundle,   it  
              automatically  calls the BATCH file "ECHOMAIL.BAT".  You  
              would place any echomail processing instructions in this  
              batch  file. This makes it easier for those that have  a  
              hard time working with batch errorlevels and  simplifies  
              your mailer batch file.

                                    Bbs Allowed

              ALLOW Humans access to your BBS. 

                                   Do Pick-Up

              This  determines  whether or not  phoenix  will  pick-up  
              anything  during an outbound call. If PICK-UP is  turned  
              off,  Phoenix will drop off what every it has  and  then  
              hang-up.
                             Maximum Request Per Event

              This  sets the maximum number of files a  remote  mailer  
              can  file  request during this event. If  you  set  this  
              field  to ZERO, you have disabled file  requests  during  
              this event.
                                      Summary

              While almost every part of CONFIG.EXE is  heavily  error  
              trapped  to  prevent mistakes, the event  subsystem  has  
              exceptionally heavy error trapping.


         Phoenix           Technical Reference Manual        Page  48


              The event subsystem has TWO types of messages, flat  out  
              ERROR messages and WARNING messages.

              An ERROR message will 'FIX' the problem. The FIX may not  
              be  want you wanted, but it will be legal. If  it  isn't  
              what you wanted, you'll have to edit the field again.

              Possible Error messages ARE:

              Ending Time Must Be Greater Than Starting Time.
              An Event Cannot Span Midnight!
              1 - 30 And 200 - 255 Reserved For Phoenix.
              Valid Starting Times: 00:00 - 23:59.

              A  WARNING  message is use to notify you of  a  POSSIBLE  
              mistake on your part. If another event is involved,  the  
              EVENT NUMBER (events are numbered starting with 1)  will  
              be displayed so you can check it out personally.

              Possible WARNING messages ARE:

              That LABLE Is Being Used By Event No. 1
              THIS Starting Time Being Used By Event No. 1
              That Control File Is Being Used By Event No 1
              That Errorlevel Is Being Used By Event No. 1
              That Batch File Is Being Used By Event No. 2
              You Have DISABLED File Requests For This Event.

              When  you  EXIT the events subsystem, CONFIG  will  SORT  
              your  events by starting time. Phoenix does not have  to  
              have  them sorted, but it will be easier on you if  they  
              are.

              If  you access the event subsystem from WITHIN  PHOENIX,  
              i.e.  Phoenix is running, any changes you make  will  go  
              into effect ASAP.

                         Request.ctl And File Requests

         File Request: A mailer calls your mailer and sends a  REQUEST  
         file containing the names of files he would like to have.  If  
         those files are available, your mailer gives them to him.

         You have to tell Phoenix  what  directories you'll allow file   
         requesting out of by making a text file called Request.ctl. 
  
         Each line in Request.ctl contains a FULL DOS PATH ending with  
         a backslash.





         Phoenix           Technical Reference Manual        Page  49

         Example:

         C:\OSIRIS\FILES\GENERAL\ 
         C:\OSIRIS\FILES\FRONT-END\ 
         C:\OSIRIS\FILES\CATNIP\ 
  
                                Password Protection
 
              To  password protect a directory, add a space  then  the  
              password, up to 80 characters.
 
              E.g.

              C:\OSIRIS\FILES\GENERAL\ 
              C:\OSIRIS\FILES\FRONT-END\ 
              C:\OSIRIS\FILES\CATNIP\ 
              C:\OSIRIS\FILES\GAMMA\ ULTRA

 
              The  directory  "C:\OSIRIS\FILES\GAMMA\"  requires   the   
              password "ULTRA".
 
              Phoenix   supports the standard wazoo method  of   doing   
              password requests, i.e., FILENAME !PASSWORD
 
              Phoenix also supports : FILENAME PASSWORD

                                  Update Requests

              Phoenix  supports standard wazoo UPDATE  file  requests.  
              That is like a normal file request except the sender and  
              receiver compare the date and time the file was  created  
              and  the sender, Phoenix in this case, would  only  send  
              the file if it is newer.

                               Minimum Request Speed

              You  can  set  a MINIMUM baud rate  for  File  Requests.  
              Access  your CONFIGURATION system and CLICK on the  MORE  
              box.

              When you get the MORE screen, you'll see a field labeled  
              "Minimum Request Speed". The default value is 0, meaning  
              anything can request if it can connect with you.

                           Requests From Unknown Systems

              You  can  restrict file requests to ONLY  those  systems  
              listed  in your nodelist. To set this option,  click  on  
              the PGDN box.




         Phoenix           Technical Reference Manual        Page  50

              When  the  second  screen appears, you'll  see  a  field  
              labeled  "Accept  F'Reqs  From  Unknown  Systems".   The  
              default  is  YES but you can TOGGLE the field to  NO  by  
              clicking on it.

                        Error Messages Sent To The Requester

              If  there  is  an  error  related  to  a  file  request:  
              exceeding  request  limits, connect rate to  slow,  etc.  
              Phoenix will, providing you define the message, send the  
              error message (in PKT format) prior to disconnecting.

              To DEFINE the messages, create the following TEXT  FILES  
              and place them in the PHOENIX ROOT directory.

              NOFREQ.001 {Sent When No Requests accepted during  THIS event}
              NOFREQ.002 {Sent When Baud Rate TO slow for REQUESTING}
              NOFREQ.003 {Sent when NO REQ's from UNLISTED SYSTEMS}
              NOFREQ.004 {Sent when the caller exceeds Maximum F'Req For 
                          THIS EVENT}

              The matrix message TO the caller is addressed as  coming  
              from YOU and going to the NAME of the sysop as listed in  
              the WAZOO or HTM header.

              The body or contents of the message will be the contents  
              of the text file(s) NOFREQ.00x.

              Several example NOFREQ.00x files have been included.  If  
              you  do  not  want to send these  messages,  delete  the  
              files.

                                 Echomail.bat

         When  Phoenix receives an echomail bundle, during an  inbound  
         or   outbound   mail  session,  it  will   attempt   to   run  
         "ECHOMAIL.BAT" after the connection has been terminated.

         Phoenix will shift to EMS or overlay itself to disk if EMS is  
         not  available freeing all but 5K of memory prior to  calling  
         "ECHOMAIL.BAT".

         You   would  create  echomail.bat  and  place  any   echomail  
         processing instructions in this batch file.

         This  simplifies processing for those that have trouble  with  
         batch errorlevels.







         Phoenix           Technical Reference Manual        Page  51

                            Mail Transfer Protocols
 
         There  are  almost  as many  different  mailer  protocols  as   
         mailers.  Almost but not quite, there are over 100  different  
         brands of mailers used in fidonet.

         Phoenix supports the following Mail Transfer Protocols:
 
                                   Xmodem/Modem7
 
              Fidonet FSC-0001 states that ALL mailers should  support   
              a  basic  Xmodem/Modem7 protocol.  This  protocol  sends  
              MATRIX messages first using xmodem and any file attaches  
              using modem7.
 
              But  Fidonet has never enforced its own regulations  and  
              you   find   a   lot   of   mailers  that  do   not   do  
              Xmodem/Modem7. 

              Phoenix is fully FSC-0001 compliant. 
 
              A number of mailers that do not support Xmodem/Modem7 do  
              support   several   variations  of   the   xmodem/modem7  
              protocol, Diet INFA and SEAlink.

                                     Diet Infa
 
              Diet  INFA  is  a "LITTLE" faster  form  of  the  FSC001   
              protocol  that uses Telink in place of  modem7.  Phoenix  
              supports Diet INFA. 
 
                                      Sealink
 
              SEAlink  is  a  method that's quite a  bit  faster  than   
              FSC001   and Diet INFA. 
 
              Phoenix  supports SEALink including extended   form   of   
              SEAlink  known as   SEAlink   with  OVERDRIVE. 
                                    Notes On Sealink

                   Because  there  is  a  CLASH  between  Spoofing  to  
                   Telink, known as DIET INFA, and Spoofing to SEAlink  
                   (They  use  the EXACT same  character  sequence  to  
                   SPOOF), You MUST have the NODELIST SESSION type set  
                   to 5 if you want SEAlink used on an outbound call.

                   If Phoenix were to go directly to SEAlink when  the  
                   SPOOF  (Don't  know  where  that  name  came  from)  
                   sequence  was received and the mailer on the  other  
                   end  actually  wanted Telink, 8 out  10  times  the  
                   transfer  will fail even though Phoenix  will  drop  
                   back to Telink in an attempt to recover.


         Phoenix           Technical Reference Manual        Page  52

                   If Phoenix is the receiver, it doesn't matter  WHAT  
                   the  sender  wants to use. It can  slide  back  and   
                   forth  between Xmodem, Modem7, Telink, and  Sealink  
                   without skipping a beat.

                   On  an  INBOUND call,  assuming  Wazoo/Internet/HMS  
                   wasn't asked for, Phoenix will use SEAlink ONLY if

                   A)  The caller has a nodelist record and it is  set  
                   to session type 5.

                   B) The caller uses Sealink FIRST.

                                       Wazoo
 
              Wazoo,  created by Wynn Wagner III, is a popular  mailer   
              protocol  and  widely implemented. It  isn't  that  much   
              FASTER  than SEAlink with Overdrive, but it  does  offer   
              several advantages over SEAlink. 
 
              The   Wazoo/Zmodem protocol built into Phoenix is  solid   
              and   fast.  Although I must admit that it took  several   
              years   of   almost constant FINE tuning, in  our  other  
              mailer,  to  get it to  talk  with  all  of  the  varies  
              Wazoo based mailers.

              Wazoo  file  requests  and  Wazoo  UPDATE  requests  are   
              supported.
 
              So   far  I've  listed ALL the major,  and  minor,  mail   
              protocols   used  by Fidonet mailers, but   despite  the   
              advantages  Wazoo  has over the other mail protocols, it  
              isn't up to snuff.
 
              The   reason   it isn't up to snuff  is  the   excessive   
              OVERHEAD   wazoo,  or  rather zmodem,  adds  to  a  file  
              transfer.

              Zmodem  uses an encoding system that can, and does,  add  
              additional overhead to a file. 

              E.g.,  if you read 8196 bytes from the file, Zmodem  may  
              expand   that to 8233 bytes and you SEND the 8233  bytes  
              instead of the  original 8196 bytes.
 
              In THEORY, Zmodem COULD double the size of the file.
 
              The  largest file we've tested using Zmodem was 340K and  
              it  was  expanded by a little over 8K. 
 




         Phoenix           Technical Reference Manual        Page  53


              The  amount varies depending on file type.   Ironically,   
              the  type  that expands the MOST is the  format  Fidonet  
              uses    to   distribute  their  official  files,   i.e.,  
              Nodelist,  Newsletter,  etc. 

                                  Turbo Charged Wazoo!

                   Phoenix  has  a built in WAZOO Turbo  Charger  that  
                   works with ANY mailer out there. 

                   The  WAZOO Turbo Charger will generally boost  your  
                   throughput  by about 3 to 5 percent over  what  you  
                   would  have gotten had you been  running  D'bridge,  
                   FrootDoor, or Binkley.

                   While the Turbo Charger does work when SENDING, you  
                   aren't  likely  to  see more than 1  or  2  percent  
                   increase in throughput because the receiver plays a  
                   BIG  role. However, you should see 3 to 5 when  you  
                   are the receiver (unless you are already running  a  
                   super fast computer).
                   

                               Highspeed Mail Session

              While  WAZOO does offer a faster "HANDSHAKE"  than  FSC- 
              0001  mail sessions, it is still fairly slow  and  often  
              fails  if it runs into line noise or delays  induced  by  
              satellite links.

              We  have developed, and used for several years, our  own  
              proprietary  highspeed mail session, simply called  HMS,  
              that  is  about  30  times  faster  when  it  comes   to  
              establishing a handshake between the two mailers.

              It is also considerably more reliable and handles  noisy  
              lines and satellite links hundreds of times better  than  
              Wazoo.
             
                                           Hsp

                   Having  developed a better HANDSHAKING system,  the  
                   thought of having to use something like Zmodem with  
                   its   excessive   overhead   and   sensitivity   to  
                   satellites just didn't make sense.

                   So  in 1988 we become development and testing on  a  
                   protocol  called HSP, HSP is short for  High  Speed  
                   Protocol.  This protocol was designed to  run  with  
                   less  than  1/2  of one  percent  overhead,  handle  
                   satellite links, networks, multitaskers, and  other  
                   items  that  induce  time delays. 

         Phoenix           Technical Reference Manual        Page  54

                   Since   1988,   HSP  has  surpassed   our   wildest  
                   expectations.  Not  only does it  handle  satellite  
                   lines, networks, and ARQ resends without batting an  
                   eye, it turned out to be the faster protocol in the  
                   world.

                   HSP  is about 5 percent faster than Zmodem at  2400  
                   baud,  10/15 percent faster at 14.4, and nearly  20  
                   percent  faster  when used  with  v.FAST  (proposed  
                   v.FAST standard. v.FAST hasn't been finalized yet) 
                   
                                    Restart Recovery 
  
                        Yes,    full     Restart      Recovery      on     
                        interrupted   transfers.   You'll  find   that   
                        restarts  are  almost  instantly done from the  
                        word GO. 

                                   Errors During A Transfer
 
                        Most   protocols do not know WHEN or even   IF    
                        the    transmitter   has   received  a  resend   
                        request.  Even   the most  popular  protocols,  
                        Zmodem,  suffer  from   this ailment. 

                        Zmodem  may actually be the worst one since it   
                        can   actually go quite  some time  before  it  
                        figures  out  that the sender did  not see the  
                        resend request. 

                        HSP  does   NOT   suffer  from   this.     The    
                        Transmitter   is always  sampling the  reverse  
                        stream   in  an  attempt   to   detect  resend   
                        requests.   If  it   does   detect   a  resend   
                        request,    it   immediately    notifies   the  
                        receiver that it has   detected   the  error.

                        At  this point, both receiver and  transmitter   
                        agree   to exactly where they SHOULD be,  with  
                        the  receiver  having  the  final  say in  the   
                        matter.   Once  the  line  has  settled,   the   
                        transmitter  will  resume  transmission at the  
                        correct spot. 
                                 How Does This Help Me?

                   If  you  are doing mail with  local  systems,  then  
                   using  HMS  and Translink will only give  your  BBS  
                   callers more time on-line.

                   However, if you are making long distance calls,  it  
                   can  reduce  your  phone  bill by  as  much  as  50  
                   percent, nothing to sneeze at.


         Phoenix           Technical Reference Manual        Page  55


                   The TYPICAL wazoo mail session to drop off a couple  
                   of  messages, drop off a small echomail bundle  and  
                   then pick-up one generally takes about 1.5  minutes  
                   (14.4 Connect).

                   Of  course,  this  is a TYPICAL  HOST  level  wazoo  
                   session.   Echo  hubs  generally  transfer   larger  
                   amounts.

                   If you use HMS and HSP you could get in and out  in  
                   less than  50 seconds and that keeps you from being  
                   BILLED for a 2 minute phone call.

                   Of course the amount of money HMS and HSP can  save  
                   you will vary from system to system.

                   The  BEST  way to optimize for HMS and  HSP  is  to  
                   simply  monitor your mail sessions to a  particular  
                   system for a couple of weeks. 

                   Look at your connect times and then for a couple of  
                   weeks cut the number of calls in half. I.E., if you  
                   are calling once a day, call once ever TWO days.  

                   Then compare the CONNECT times. You will more  than  
                   likely find that you can save money by cutting  the  
                   number  of calls with HMS and HSP because  you  can  
                   transfer  nearly twice as much data in  that  first  
                   minute.

                   Of course, if you use a long distance service  that  
                   bills in 10 second blocks (some SPRINT LD  services  
                   offer  this option), you'll find that  you'll  save  
                   even more.

                                        Emsi

              EMSI  is  pretty much like your standard WAZOO  only  it   
              uses   a   different  method  of  passing   the   system  
              information. After the system info has passed, the  file  
              and message transfers generally revert to Wazoo's ZEDZAP  
              or  Phoenix's  HSP protocol. 

              EMSI does have several weak points, it isn't always data  
              secure and it does pass a lot of redundent information.

              It can also COST more to do an EMSI session  because the  
              packing  of  mail cannot take place until  the  PHYSICAL  
              connect  has been established. You don't really KNOW  in  
              advance  how many addresses you will run into  when  the  
              connect  is  actual made. You only know  about  the  ONE  
              address that was used to trigger the call.

         Phoenix           Technical Reference Manual        Page  56

              A  better  alternative is to use ROUTING  and  a  single  
              pickup address, explained below.

                                   Outbound Emsi 

              If  you  want to Phoenix to use EMSI when you  place  an  
              outbound  call, you have two options. You can  toggle  a  
              systems nodelist session type to EMSI or you can  toggle  
              "Session  Type ANYTHING Includes EMSI", To YES.

              The preferred method, toggle the nodelist record to EMSI  
              because  that prevents you from falling into  a  session  
              type that may use a protocol that is slower than Zmodem. 

                                    Inbound Emsi

              The default is not to allow EMSI on inbound. If you want  
              to  allow inbound EMSI, then toggle Allow Inbound  EMSI,  
              config,  to  YES. 

              With the ability to route files and anything else,  it's  
              more  cost  and time efficient to use HMS  or  WAZOO  in  
              conjunction with ROUTE TO 

                                    Secure Emsi

              EMSI  uses a single password to cover all the  addresses  
              passed in the EMSI header. For total security, you would  
              have  to  pull up the nodelist record for  each  one  of  
              those  addresses and compare the passwords to make  sure  
              they  ALL  match. Several EMSI mailers do not  do  this.  
              They  use the primary address and compare  the  password  
              with only that record. 


              If you toggle Secure EMSI on, config, Phoenix will check  
              every  single address to make sure the passwords  match.  
              Under  normal  conditions,  Phoenix can do  this  at  an  
              exceptional  fast rate, about 1/10th of a second per  20  
              AKA's. 

              There  are  conditions  that  might  arise  that   could  
              drastically  slow  this  down,  like  running  across  a  
              network  server. Because we don't know what  your  exact  
              setup is, you'll need to decide if you want  or can  use  
              SECURE EMSI.

              Keep  in mind that you do NOT have to use EMSI  to  hand  
              off or pickup mail under multiple addresses.





         Phoenix           Technical Reference Manual        Page  57

              Example:

              9.999.10.0   belongs   to  XYZ  net   and   to   Fidonet  
              1.237.504.0.  

              Add the following line to your event:
 
              ROUTE 9.999.10.0 To 1.237.504.0

              When 1.237.504.0 calls to pickup Fidonet echomail, he'll  
              also get any XYZ echomail going to 9.999.10.0

              This  doesn't pass redundant information and it is  VERY  
              fast,  it's all done BEFORE the call is ever  placed  or  
              received.  The mailers don't have to attempt to  get  it  
              all  together while the phone companies  billing  meters  
              ticking  away,  like  they would under  EMSI.  
         
                                 Matrix Editor

         The  Phoenix matrix editor is PED.EXE. You can call  it  from  
         within Phoenix  by pressing ALT-E, E for EDITOR.

         The matrix editor is responsible for keeping the matrix  area  
         contingent, i.e. 1.MSG 2.MSG 3.MSG 4.MSG etc.

         When  you  first  run PED, you'll get  a  "Please  Stand  by"  
         message,  PED  is renumbering the messages.

         The primary PED display screen isn't THAT fancy, although  it  
         is pleasant to look at and informative. We decided to go with  
         the  LARGEST text display window, the body of the message  is  
         displayed here, we could get: 16 lines by 80 columns.

                               Message Movement Keys
          
              Left  and Right arrow, moves you backwards and  forwards  
              (respectively).

              HOME, takes you to the FIRST  message.

              END, takes you to the LAST message.












         Phoenix           Technical Reference Manual        Page  58

                           Movement Keys, Viewing Message

              When  you are reading a message you have  the  following  
              movement keys:

              PgUp - Self Explanatory
              PgDn - Self Explanatory
              Up Arrow - Scroll UP a line.
              Dn Arrow - Scroll DN a line.
              CTRL-PgUp - TOP of message.
              CTRL-PgDn - BOTTOM of message.

                                    Command Keys

              A  - Edit CURRENT Message
              E  - Enter A Message
              F  - Forward CURRENT Message
              C  - Carbon Copies
              R  - Reply To CURRENT Message
              K  - Kill Current Message
              F1 - Display Kludge Lines.
              F9 - Cipher Block A Message Or File.
              F0 - Decode A Cipher Blocked Message Or File.
              ESC - Exit PED
              ALT-H  Help

                                    E - Enter Message
                   When you enter a message, you have to tell PED what  
                   TYPE of message you're going to enter.

                   [M]sg  - This is just a PLAIN message.
                   [F]ile - This is a Message that will have  a  FILE  
                            ATTACH.
                   [R]eq  - This is going to be a FILE REQUEST.
                   [S]rv  - This is going to be a SERVICE REQUEST.

                   If you press ENTER, [M]sg will be used.

                   The next step is ATTRIBUTES (How Phoenix is suppose  
                   to TREAT the message).

                   You have FOUR options:

                   [C]rash
                   [D]irect
                   [K]ill
                   [H]old







         Phoenix           Technical Reference Manual        Page  59

                   Press  the  FIRST letter to  select  an  attribute,  
                   press ENTER when you are done.

                   PED  will  TRAP  mistakes  during  this   selection  
                   process  and  will  not  allow  you  to  select  an  
                   attribute  that doesn't fit the TYPE of message  or  
                   an attribute that conflicts with another ATTRIBUTE.

                   For instances, it will not allow you to use [C]rash  
                   and  [H]old together. It will not allow you to  use  
                   [K]ill  with  a  FILE REQUEST  or  SERVICE  REQUEST  
                   (Those TYPES are automatically flagged as KILL).

                   Once you have selected the message TYPE and message  
                   ATTRIBUTES,  PED will ask you for the NAME  of  the  
                   person the message is addressed to. 

                   If  you  are  NOT replying to a  message  PED  will  
                   attempt to FIND a nodelist record that matches  the  
                   name in the TO field. If it finds a record, it will  
                   display the record and ask you if it is the CORRECT  
                   record. 

                   Because   of   the  SIZE  of  the   nodelist,   the  
                   SYSNAME  index is used and does require  a  perfect  
                   match. If you are not SURE of the spelling and  you  
                   don't KNOW the domain address, you can have PED  do  
                   a slide match lookup by ending the name with *

                   Eg. John kl*

                   Be  forewarned, the highspeed INDEX cannot be  used  
                   and PED will have to scan the nodelist data records  
                   themselves  so this is a lot slower. You CAN  abort  
                   the scan at any time by pressing ENTER or the SPACE  
                   bar.  
                    
                   PED  will then attempt to validate the TO  address.  
                   If  it  can't,  it  will ask you  if  you  want  to  
                   continue. There are a few valid reasons WHY Ped may  
                   not be able to validate the address:

                   1. You are using a FULL ROUTING nodelist.
                   2. You may be sending it to a POINT system.
                   3. You may be sending it to a different NETWORK.

                   The  next  step is the FROM name  field.  PED  will  
                   place  the name of the person who OWNS the  mailer,  
                   defined  in your phoenix config, in this field.  If  
                   you  want  to keep it, press ENTER. If  you  don't,  
                   press ESC and type in the name.



         Phoenix           Technical Reference Manual        Page  60

                   The  final  step is the subject. If it  is  a  file  
                   attach, enter the full drive, path, and file  name.  
                   If  it  is  just a plain  message,  enter  a  short  
                   subject.

                   If you are sending a file request, type in the name  
                   of  the file you want to request and  press  ENTER.  
                   The subject line will clear and you can continue to  
                   type  in  the names of files you want  to  request.  
                   When  you  are done, press ENTER  without  entering  
                   anything.

                   If  you  are doing an UPDATE request,  be  sure  to  
                   include the full drive, path, and file name to  the  
                   file on YOUR system.

                   If you are doing a file request and already HAVE  a  
                   REQUEST going to that system, PED will NOT create a  
                   NEW one. It will append to the exiting  REQUEST  
                   file.
                              R - Reply To Current Message

                   Reply  works  a  lot like Enter with  a  few  minor  
                   exceptions.

                   The  text  TO  and Destination  DOMAIN  are  filled  
                   according  to  the  TO and  ORIGIN  DOMAIN  of  the  
                   message you are replying TO. You do have the option  
                   of editing both fields.

                   The  SUBJECT of the message you're replying  to  is  
                   copied to the REPLY message, you have the option of  
                   editing.
                                K - Kill Current Message

                   This  deletes the CURRENT message. If that  message  
                   had  a  file attach and that attach was  marked  as  
                   KILL, the attached file will be deleted as well.

                   After  deleting the message, PED will renumber  the  
                   messages to fill in the HOLE.

                                       F - Forward

                   This  lets  you  FORWARD  the  CURRENT  message  to  
                   another individual.

                   You will be asked to fill in the TO and Destination  
                   message's Date, Subject, and Attribute fields. 

                   Your  name and Domain address will be used  as  the  
                   SENDER.


         Phoenix           Technical Reference Manual        Page  61

                                       C - Carbons

                   Carbon  lets you send CARBON copies of the  current  
                   message to other individuals.

                   The  CARBON function uses a TEXT Control file  that  
                   should contain the ADDRESSES of the people you want  
                   to send CARBONS to.

                   The Format of the control file is:

                   ZONE.NET.NODE.POINT
                   ZONE.NET.NODE.POINT

                   etc.

                   A  full domain address, one per line. There  is  no  
                   limit on the number of lines in the control file.

                   To use CARBONS, enter the FIRST message to  someone  
                   listed  in  the control file. After  you  save  the  
                   message, move to it and press 'C'. 

                   A  window will open and you'll be asked  to  supply  
                   the  name of the control file that  containing  the  
                   address list. 

                   A  CARBON of the message will be sent to  everyone,  
                   except  the  person  you  used  for  the   original  
                   message, listed in the control file.

                   You MUST have a nodelist record for each individual  
                   listed in this control file.

                                A - Edit Current Message

                   Lets you edit the current message.  

                                K - Kill Current Message

                   Delete   the  current  message  and  renumber   the  
                   remaining messages.

                                   F1 - Display Kludge

                   Messages  sometimes  contains  hidden  lines   that  
                   effect  the  way  mailers, in  general,  and  other  
                   applications deal with a message.

                   We  generally  hide  them because they  are  of  no  
                   interest  to the end user. However, if you do  want  
                   to look at them, press F1.


         Phoenix           Technical Reference Manual        Page  62


                                    F9 - Cipher Block

                   Ped  contains a very sophisticated data  encription  
                   system,  sometimes  called DES or  Ciphering.  This  
                   allows  you to encode a message, or file,  so  only  
                   those  with  the proper CIPHER keys  can  read  the  
                   message or use the file.

                   There  is no need to go into exactly what  type  of  
                   DES/Cipher  system we use, although it would do  no  
                   harm to tell you, since it is fairly complex. 

                   Instead,  let  me  just  say that  it  is  all  but  
                   unbreakable. Even knowing the method and having the  
                   code, we cannot break any message or file that  you  
                   Cipher Block with PED.

                   It,  like anything, is not TOTALLY  unbreakable.  A  
                   super computer running non-stop for about 500 years  
                   "MIGHT" be able to break the cipher, but we'll  all  
                   be  dead and buried by then so who cares. There  is  
                   also pure luck but you'd have better luck  becoming  
                   the president of the United States, as if anyone in  
                   the right mind would want that.

                   When  you press F1, PED will ask you for  a  Cipher  
                   Key.  This is used to encode the message  or  file.  

                   Anyone wanting to read the message or use the  file  
                   MUST decode the message or file with the exact same  
                   key.

                   Cipher  keys  can be up to 25 characters  long  AND  
                   they are case sensitive. In other words, "RADIO" is  
                   NOT the same as "radio".


















         Phoenix           Technical Reference Manual        Page  63


                                    Dc Word(tm)
 
              DC   Word(tm)   isn't actual  an   individual   program,   
              it's a  module for Message entry.

              DC    Word(tm)    was   designed    specifically     for   
              message   entry    systems   found    in   CBIS,    BBS,   
              Mailers,   etc.   It has many, if  not   more,   options   
              found in most popular word processors.

              DC Word(tm)  has  a default left margin of one  and    a    
              right   margin   of  75.  The  margins   may   not    be   
              changed.
  
              When  entering test, I'll automatically wrap   when  you  
              exceed the 75th column.

              If    you   press <CR> then you'll move  to   the   next   
              line, if  one is  available, and the line you where   on  
              will  be   flagged   as  ENDING  with  a  HARD  CARRIAGE   
              RETURN.

              DC  Word(tm)   allows up to 161 lines  of  text,   seven    
              pages    or   about  13K.  There   are   other   systems    
              that  cannot  handle messages exceeding 10K.

              At   the   bottom of the screen you'll  find  a   status    
              bar.   It  shows the current row, col., page,  and   the   
              number of lines left, excluding  the current line.

              There    are   several command  keys    available    and   
              pressing  ALT-H will display  a  help   screen   listing  
              them.

                                      Command Keys

                   Items   beginning  with  (*)   designate   wordstar   
                   compatibility. 

                   (*) Up Arrow Key or ^E - Move up a line. 

                   (*)  Dn Arrow Key or ^X - Move down a line  (cannot   
                   go  pass last line of text). 
 
                   (*)  Left Arrow Key or ^S - Move one  CHARACTER  to   
                   the left. 

                   (*)  Right Arrow Key or ^D - Move one CHARACTER  to   
                   the right.

                   (*) Ctrl - Left Arrow Key or ^A - Move one WORD  to   
                   the left. 

         Phoenix           Technical Reference Manual        Page  64

                   (*) Ctrl - Right Arrow Key or ^F - Move one WORD to   
                   the right. 

                   (*) HOME or ^Qs - Move to the start of the  current   
                   line. 

                   (*)  END  or ^Qd - Move to the end of  the  current   
                   line. 

                   (*)   Ctrl-HOME  or ^Qr - Move to the  first  line,   
                   first  column of the message. 
 
                   (*) Ctrl-END or ^Qc - Move to the Last line,  first   
                   column of the message. 
 
                   Ins   -  Toggles Insert Mode on/off. Cursor becomes    
                   a  BLOCK when in insert Mode.
 
                   (*)  DEL  or ^G - Delete the  character  under  the   
                   cursor, move rest of line back to fill hole. 

                   If you are at the end of the line, I'll look at the   
                   line below your current position and if I can  move   
                   text from that line to your current line, I will.
 
                   (*)  PgUp  or  ^R -  Move up a page or  to  Top  of   
                   document, which every comes first. 
 
                   (*) PgDn or ^C -  Move down a page or to Bottom  of    
                   document,  which every comes first. 

                   (*)  Ctrl-N    -  Split the line  at  the   current    
                   cursor  position. 

                   (*)  Ctrl-Y   - Delete the current line,  move  all   
                   text up a  line. 

                   (*) Ctrl-I   - Tab 

                   (*) BS       - Backspace delete. 

                   ESC      - Done editing, exit DC Word(tm). 

                   (*) Ctrl-B   - Reformat document. 

                   ALT-D    - Engage Dictionary.

                   ALT-J    - Jump to DOS. 

                   ALT-I    - Import Text file. 
  
                   ALT-X     - Delete from current position to end  of   
                   line. 

         Phoenix           Technical Reference Manual        Page  65

                   ALT-S     - Cursive Signature.
         
                   ALT-R    - Redraw Screen. 

                   (*) ^KB  - Start Block Mark. 

                   (*) ^KK  - End Block Mark. 

                   (*)  ^KC  - Copy Marked text to line below  current   
                   location. 

                   (*) ^KY  - Delete Marked text. 

                   (*) ^KH  - Dissolve Block Marks (HIDE). 

                   (*) ^KW  - Write Marked text to a file. 

                   Marked    Text  will  be  highlighted   in  reverse   
                   video. This is to illustrate what has been marked.

                   (*)  ^U   - Undelete last line  deleted  with  ^Y,   
                   Delete  buffer will  hold the last 36 lines of text    
                   deleted  with ^Y.  Individually  deleted characters    
                   will  NOT  be saved in the un-delete buffer.
 
                   (*) ^T - Delete word. DC Word(tm) will start at the   
                   current cursor position and delete an entire  word.   
                   The end of the word is denoted by either end of the   
                   line,  a  white  space, or a  punctuation  mark  is   
                   found. 

                   If  you are at the END of the line to  start  with,   
                   WORDS  that will fit in the remaining space on  the   
                   next line will be pulled up to the current line.
 
                   ^V - Insert Blank line below current position. 

                   ALT-C  - Access Cut section of CUT/PASTE.  Requires   
                   Mouse. 

                   ALT-P   -  Access  Paste  section   of   CUT/PASTE.   
                   Requires Mouse.

                   <- Del Key - Moves the cursor back a character  and   
                   deletes  the character at the new cursor  position.  
 
                   If  you're at the start of the line, I'll move  you   
                   to  the end of the line above you and pull as  many   
                   WORDS up to the line that will fit. 

                   Right  Mouse Button - Active Quick  Jump.  Requires   
                   Mouse. 


         Phoenix           Technical Reference Manual        Page  66

                   All  functions  will  prevent you from going   pass    
                   the   last available  line. Should you attempt  it,   
                   the system will  BEEP at you. 
 
                   Alt-J Jump To Dos.  This   uses  VMS to free up all   
                   available   memory.    The    current  screen   and  
                   cursor positions will  be  saved and restored  when  
                   you return.

                   If  I can't allocate a buffer to store  the   video   
                   screen, you'll get an error message and the Jump to   
                   DOS  will be aborted.
 
                   Ctrl-B Reformat.  After   a  heavy editing session,  
                   your   text   could  look    choppy.  This   really  
                   doesn't hurt  anything,  but it's there if you want  
                   to use it.

                   Alt-I  Import File. Allows   you  to  import   text   
                   files.    The   only   restrictions placed on  this  
                   function  is  the size of  the  file. It  must  fit  
                   within the space you've  got  left. I'll make  sure  
                   of that and when you run  out  of space, I'll  quit  
                   importing the text.

                   Although  it's not a restriction, the length of the   
                   lines  in the file should be discussed. 

                   I'm  allowing  only 78 character  per  line  before    
                   either   wrapping or requiring  a   HARD   CARRIAGE   
                   return.  Should   the  file   contains  lines  that    
                   will  not  meet  this requirement,  I'll force   it    
                   by  placing  HARD CARRIAGE  returns in as needed. 

                   This means a file may not look like you  though  it   
                   would. 

                   If  you're  importing files that have lines  LONGER    
                   than  66 characters,  I  suggest  that you  attempt    
                   to  shorten  them so they'll display correctly. 

                   When  IMPORT is selected, you'll be asked  for  the   
                   file name. You can enter the full drive, path,  and   
                   file name, wild card characters are allowed. 

                   I'll  scan that directory and show you  a  list  of   
                   files matching the file name pattern you typed in. 

                   Move to the one you want and press return.





         Phoenix           Technical Reference Manual        Page  67
         
                   When I start importing a file, I'll always check to   
                   see if you're on a BLANK line. If not,  I'll  start   
                   INSERTING  the text following  the  line you're on.   
                   I'll NEVER  over  write  any existing line of text.
 
                   Alt-S,  Cursive Signature. Press  ALT-S, enter  the  
                   signature,  and it  will  be  converted    to   the   
                   new  FONT format and  you  may  place it   anywhere   
                   in  the message by pressing the  ALT-P for paste.

                   You  can  also  block mark the signature, once   it    
                   has   been displayed with ALT-P, and write it to  a   
                   MACRO file.

                                        Cut 
  
              Allows you to mark text on the screen and places it   in    
              a  buffer.  Cut  does NOT remove or delete  the   marked    
              text.    It cuts  out  a   section  of  the  screen  and  
              store  it  for  PASTE recall.
 
              Once   this   option  has been   selected,  ALT-C,  your   
              mouse   cursor  will  be placed in  the  middle  of  the   
              screen.  Move  to  the   upper  right  hand  corner   of   
              the  section  you want to cut and press the  LEFT  mouse   
              button. This will drop the first anchor. 

              Once the first anchor has been dropped you may  not   go  
              pass it, horizontally or vertically. 

              As   you   move, the text will  be  highlighted.    Once    
              you    have   selected  all that you  wanted   to   CUT,   
              press the  RIGHT  mouse button. 

              You   can   CUT  as little as one   character   or   the   
              entire   screen.  If  you  cut  multiple  screen  lines,   
              then   each   line  will  end with   a   hard   carriage   
              return.   The    text will remain in  the   cut   buffer   
              until  you   select  to CUT more text. 

                                       Paste 

              Press ALT-P to activate Paste.

              If    you  have CUT text, selecting  the  PASTE   option   
              will    begin   placing the text in  your   message   at   
              your   current  location. If you  are  NOT   in   insert   
              mode   and   you aren't at the end   of    the   message    
              then    the    text that's already   there    will    be    
              over written. 




         Phoenix           Technical Reference Manual        Page  68

              You   can  paste CUT text as many times  as  you   like.    
              The    same   text will be available   until   you   CUT   
              more. 
                                     Quick Jump 

              Quick    Jump   is activated by   pressing   the   RIGHT   
              mouse   button.  This allows you to  QUICKLY   jump   to    
              different    spots   in  your   message,   limited    to   
              locations  on the CURRENT screen. 

              When   you  press the RIGHT mouse  button,   the   mouse   
              cursor    will   be   placed in  the   middle   of   the   
              screen.  Move to the  location you want to jump  to  and  
              press the LEFT mouse button.

              You   can't  move pass the last line of  text   or   the    
              last  column   on a particular line.  Attempts  to  move   
              pass  the   LAST line  of  text will place  you  ON  the   
              last line.  Attempts  to move pass the last  column   on   
              a  particular line will place you at  the  LAST   column  
              position for that line.
 
                                       Macro Keys

              You have 9 scrap MACRO keys that can be  programmed   to  
              do all most anything you can do manually. 

              Each MACRO can be triggered by pressing ALT-1  - ALT-9. 

              Providing   the   MACRO file for that  key  exists,   it    
              will  be executed. 

              Each   MACRO  has its own specific  command  file,  MACx   
              with  x being  the   MACRO key in question. 

              i.e. MACRO ALT-1  uses  the file name MAC1 

              To    create  a MACRO file, use any  text   editor   and    
              enter   what  you  want. Normal text,  not  DC  Word(tm)   
              commands,   will    simply   be   imported   into   your   
              message as TEXT. 

              All   DC  Word(tm) normal key  functions,  Ctrl-I   type   
              keys,   can   be  triggered   by    entering   them   in   
              character  format.  In  other words,  use some type   of    
              program,    like    Char.exe,    to     generate     the   
              character  representation of the ASCII  value   for  the  
              command. 

              Certain    DC   Word(tm) commands do   not   use   ASCII    
              characters   but    use IBM   Extended   Keyboard   Scan   
              codes. 


         Phoenix           Technical Reference Manual        Page  69
 
              e.g. The  Left,  Right, Up, and Down Arrow  keys. 

              Using   these   commands requires  a    TWO    character   
              sequence.   Each  command is prefixed  with  the   ASCII    
              character  238 which would look like n  Following    the   
              ASCII  238,  enter  the  character  representation   for   
              the key.

              Below  is    a   chart listing each  command   and   its    
              ASCII  value, keeping in mind that you don't  enter  the   
              ASCII value but  the ASCII character for  that  value.

              01 - Pause for 1 second 
              02 - Wait for a key press 
              45 - ALT-X, Clear to EOL 
              19 - ALT-R, Redraw Screen 
              35 - ALT-H, Show Help 
              36 - ALT-J, Jump to DOS 
              23 - ALT-I, Import Text File 
              82 - Toggle Insert on/off 
              83 - DEL, Black hole delete 
              77 - Right Arrow key, move right one character. 
              75 - Left Arrow Key, move left one character. 
              115 - Ctrl-Left Arrow Key, move left a word. 
              116 - Ctrl-Right Arrow Key, move right a word. 
              73 - PgUp 
              81 - PgDn 
              119 - Top of Document 
              117 - End of Document 
              72 - Up Arrow 
              80 - Dn Arrow 
              79 - Goto End of Line 
              71 - Goto Start of Line 
              
              There's   no   limit to the size of  the   MACRO   file.    
              Since there's no size restriction on a MACRO, there   is  
              NO need  to allow MACRO chaining. 

 
                               Service Requests 
  
         A service request is an external process not directly related  
         to the mailer. 

         To  do a service request, just build a text file and use  the  
         filename:  SERVICE.SRV 
  
         NOTE:    In    this   file,   replace    all  occurrence   of  
         "SERVICE"  when  used   as part   of  a filename   with   the    
         ACTUAL name  of  the service. The contents of this file  will  
         vary depending on the  service you're requesting. 



         Phoenix           Technical Reference Manual        Page  70

         File   attach  the *.SRV file to that system. Make  SURE  you   
         use a file attach and NOT a file request. 

         When   I  receive one of these files, I'll  take  the   first   
         eight   characters   of  the filename, or  until  I   hit   a   
         period,   and   look  in your root directory   for   a   file   
         called SERVICE.DEF. 

         I'll  read  that file for a matching name and if I  find  the   
         service   name  listed, I'll signal the other  end   that   a          
         service  request  is about to take place and  to  extend  the   
         timeout period to 5 minutes instead of the normal 30 seconds. 

         I'll  call that program and passing the full  drive/path  and    
         filename  of  the *.SRV file on the command line.  What   the   
         program   or  batch file does, well that's up to  you.  After  
         you exit  the service program or batch file,  I'll look   for   
         a file called "SERVICE.RPT," replace  the  SERVICE  part   of  
         the name with the actual name of the service, in your Phoenix    
         root  directory. If it exits, I'll send  the  file  back   to    
         the caller. 
 
         The  contents  of  the file is up   to   the  service  you've   
         requested.  It  can  contain  text,  be  an  archive,  or  an   
         executable program. 

         Lets  say  I setup a service on my system, at   work,  called   
         "NEWNODE." The actual NEWNODE service program is a batch file   
         that  takes my  current  FIDOLIST.DAT file and places it   in    
         an  archive called "NEWNODE.RPT." The actual batch file to do   
         this . . . 

         copy con NEWNODE.BAT <RETURN> 
         pkzip -a newnode.rpt FIDOLIST.DAT  
         ^Z 

         Now,   if   I'm  at home and I want   the   latest   compiled  
         FIDOLIST.DAT  file,  all  I have to do is make  a  text  file  
         called "NEWNODE.SRV" and file attach it to my system at work. 

         When  the  system  at work receives  the  NEWNODE.SRV,  it'll   
         execute  the newnode.bat file, which makes  the   newnode.rpt   
         archive  containing the compiled FIDOLIST.DAT file, and  send   
         it back to me. 

         Phoenix would pass the command line  "C:\INBOUND\NEWNODE.SRV"   
         to  the    batch  file, but since it's a batch and  I   don't    
         need   that information,  newnode.bat  will ignore   it.   It  
         COULD be  processed with the %1 if  you wanted to do that. 





         Phoenix           Technical Reference Manual        Page  71

         To  add services to your system, just create or edit  a  text   
         file called "SERVICE.DEF."  Enter the name of the service, up   
         to 8 characters, one service per line. 
  
         There is no limit on the number of services you can have  and  
         no  limit placed on what the service can do,  within  reason.  
         Since  there  is an open file, Phoenix.log, I  would   reframe   
         from  triggering any disk compression programs or  chkdsk  /F   
         type programs.

                                 Programmers Notes 
  
              If you're going to be writing external service programs,    
              you can   require  any  type  of  data  or   information    
              in    the SERVICE.SRV file. I'll pass the  location  and   
              filename of the *.SRV to your program. It's up to you to   
              process the contents, if any, of this file. 

              The   contents   of   the  SERVICE.SRV   file   can   be    
              structured  binary,   text line formatted,  or  anything   
              else you  might  be comfortable working with. If  you're   
              going to use a structured file, you'll need  to  provide    
              a program capable of creating  the  *.SRV file. 

              If  you want your program to send anything back  to  the   
              caller, you must use the filename SERVICE.RPT. 

              Keep  this  in mind, I'll ONLY wait 5 minutes   for  the   
              completion of the service. If you take longer than that,   
              I'll disconnect. 

              If  you  have an HST, make sure the you've set  the  S19   
              register  to at least 7 so  the modem will  not  timeout   
              during a   service request. 

                                Nodelist Editor

         The  PHOENIX  nodelist editor, NED, lets you   View,  Search,  
         Edit, and ADD nodelist records.

         NED does REQUIRE a mouse to EDIT but not to VIEW or SEARCH.

         You can access NED from within Phoenix by pressing ALT-N.  If  
         you  want to access NED from DOS, just type NED from the  DOS  
         prompt.

         When  NED  comes up it checks for  NODELIST.DAT,  DOMAIN.IDX,  
         SYSNAME.IDX,  BBSNAME.IDX, HMS.IDX, and finally  PREDIAL.DAT.  
         If  any of the files are missing, NED will create  the  file. 
 
         The only exception is DOMAIN.IDX. If NODELIST.DAT exists  but  
         DOMAIN.IDX does NOT, NED cannot continue.


         Phoenix           Technical Reference Manual        Page  72

         If NODELIST.DAT does NOT exist, NED will create  NODELIST.DAT  
         and  all  IDX files. The FIRST record will  be  YOUR  record,  
         based   on  the  contents  of  your  PHOENIX.CMD   file.   If  
         PHOENIX.CMD doesn't exist, NED will exit.

         There  is a MOUSE CLICK menu that runs across the  bottom  of  
         the screen containing:

         ----->   
         <-----
         FIRST
         LAST
         ADD
         FIND
         EXIT

         To  select, move the mouse cursor to the BOX and  click  LEFT  
         mouse button.

         The mouse menu options also have HOTKEYS.

         MOUSE                         HOTKEY

         ------>                       RIGHT ARROW KEY
         <------                       LEFT ARROW KEY
         FIRST                         HOME KEY (Key pad)
         LAST                          END KEY (Key pad)
         ADD                           A
         FIND                          F
         EXIT                          ESC


         To  EDIT  a field, move mouse cursor to the field  and  click  
         LEFT mouse button.

         The  fields: Modem Type, Echomail, CM, and Session  Type  are  
         CYCLE  fields.  In  other  words,  they  CYCLE  to  the  NEXT  
         selection when you click on them. Continue to CLICK until the  
         field contains the data you want.
         
         Certain fields are REQUIRED. If you edit one of those  fields  
         but leave it blank, the ORIGINAL contents will be restored.

         All  HASH INDICES are automatically updated if you change  an  
         INDEX field.

         The  PREDIAL.DAT file is automatically updated when you  add,  
         edit,  or  CLEAR a system's PREDIAL string. If  you  CLEAR  a  
         predial, the PREDIAL.DAT record for that system is BLANKED. 

         REASON:  It cannot be totally removed because everything  is  
         POSITION  sensitive  and the ENTIRE nodelist.dat  file  would  
         have to be REINDEXED (could be very time consuming). 

         Phoenix           Technical Reference Manual        Page  73

         While  we're  on the subject of  position  sensitive,  you'll  
         notice there is no DELETE option. Since the HASH indices  are  
         all based on the NODELIST.DAT record POSITION for each entry,  
         deleting a record from NODELIST.DAT would throw all the  HASH  
         indices  off and they would have to be rebuild from  scratch.  
         It would be to time consuming to PACK a 1.8 Meg Nodelist  and  
         then  rebuild all 4 HASH indices. It would also create a  lot  
         of  disk  fragmentation.  

                                        Add

              When  you ADD a record, you'll be required to  fill  out  
              the  following  fields: ZONE, NET, NODE,  POINT,  SYSOPS  
              NAME, BBS NAME, and the PHONE.

              NED takes care of making SURE you fill out those  fields  
              and  once  you  have,  the  record  will  be  added   to  
              NODELIST.DAT and the INDICES updated.

              You  can customize the remaining fields by pressing  END  
              to  reach the NEW record and then select the fields  you  
              want to edit with the mouse.

                                        Find

              You  can  quickly locate an individual record  with  the  
              Find option.

              When  you select Find, you'll be asked HOW you want  the  
              search  done.  You have: (D)omain, (S)ysop  Name,  (B)bs  
              Name, and (P)attern Matching.

              Once  you have made your selection (D, S, B, or P),  NED  
              will  ask  you for the KEY. This is the  information  it  
              uses  during  the  search. If you select  D,  enter  the  
              DOMAIN address. If S, enter the SYSOPS NAME, etc.

              D,  S,  and B make use of the HASH Indices to  find  the  
              record so you have to be specific and enter the KEY just  
              like it would appear in the nodelist record.

              E.g. You want to find 1.237.504.0

              Select Find, press D, then enter 1.237.504.0

              If the KEY can be found, the search is VERY fast, you'll  
              be placed on the record.

              P,  pattern  matching, searches the SYSOP NAME  and  BBS  
              NAME  fields.  Since this is a RECORD by  RECORD  string  
              search, it can take a little time.



         Phoenix           Technical Reference Manual        Page  74

              When each match is made, NED will ask (after  displaying  
              the record) if this is the one you want. If it is  press  
              Y, other wise press N. To terminate the search, press  Y  
              to except the current record.

              The remaining Mouse Menu options are self explanatory.

                                   Log File

         Phoenix   keeps  a  VERY  extensive  log   detailing   almost  
         everything  that  it does. If you have a problem,  CHECK  THE  
         LOG.
                           Errorlevels & Error Msgs

         Phoenix uses several errorlevel when it needs to EXIT to your  
         batch file. Below is a list of the errorlevels Phoenix uses.

         Errorlevel           Reason

             1                You Requested The Exit.
             2                Internal Error.
             3                Received TNT Mail Packet.
             4                Received TNT Upload.
             5                Received TNT Msg Center Attach.
            11                Error Opening or Creating a File.
           255                Human Caller.

         With  errorlevels  1,3,4,  and 5.  The  following  text  will   
         appear in your log.

         Operator Requested ShutDown, Exiting Errorlevel 1
         Received TNT Mail, Exiting Errorlevel 3
         Received TNT File Attach, Exiting Errorlevel 4
         Received TNT Msg Center Attach, Exiting Errorlevel 5

         With errorlevel 2, internal Error, the following will  appear  
         in your log to explain the problem.

         (1) COMPORT.DAT Is Missing.
         (2) Could Not Allocate Ring Buffers.
         (3) Could Not Install Serial Driver.
         (4) PHOENIX.CMD Is Missing.
         (5) Modem Not Responding.
         (6) NODELIST.DAT Is Missing.
         (7) DOMAIN.IDX Is Missing.
         (8) FKEY.DAT Is Missing.
         (9) MAGIC Is Missing.
         (10) PHONE.CTL Is Missing.
         (11) Unrecoverable DOS Error.
         (12) Could Not Initialize Virtual Memory Manager.
         (13) Unknown Error, CODE XX



         Phoenix           Technical Reference Manual        Page  75

         If you ever get the last one let us know along with the  CODE  
         number so that we can trace down our mistake.

         Message  No.  11  means that DOS has  issued  an  error  that  
         Phoenix  could  not  correct. Most of the  time,  Phoenix  is  
         capable  of overriding DOS and "FIXING" whatever it  is  that  
         DOS  is bitching about. However, there are SOME  things  that  
         just can't be FIXED while the program is RUNNING. 

         It  is  up  to you if you want to cycle back to  the  top  on  
         ERRORLEVEL #2. If you do, Phoenix will try to FIX the problem  
         again.

         Message  No.  12 is issued when the  virtual  memory  manager  
         fails. If you have XMS or EMS installed, this could mean that  
         you  had an XMS or EMS driver or hardware failure. You  might  
         also check to see if the PHOENIX.SCR file is missing.

         The virtual memory manager loads the contents of  PHOENIX.SCR  
         into  XMS,  EMS,  or  Conventional memory.  If  the  file  is  
         missing, it will not be able to allocate the proper amount of  
         memory and this can cause the error.

         You may also see several other error messages in your Phoenix  
         log  and  on the screen. These error messages  do  not  cause  
         Phoenix to exit.

         Here are some of the error messages (the text of the  message  
         may  vary a little bit) you're most likely to see, there  are  
         others but they are pretty self explanatory and we don't want  
         to waste a lot space here.

         "Error,  no program was executed during Spawn!" This  message  
         would  appear when you SHELL to the BBS or execute  an  EVENT  
         batch file and NOTHING was executed during the spawn.

         "Route  File For This Event Is MISSING!"  This message  would  
         appear when you have an active event and you defined a  route  
         file and PHoenix couldn't find the file you defined.

         "Route  Cmd 'xxxxxxxxxxx'?" This would appear when  you  have  
         defined a route file for a specific event and Phoenix found a  
         command  that  it  did not understand.  'xxxxxxxx'  would  be  
         replaced with the command it didn't understand.

                                 Human Callers

         There are two methods of passing HUMANS to your BBS.

         The first and preferred method is the SHELL option. When  you  
         SHELL to the BBS, Phoenix will shift to EMS or overlay itself  
         to DISK to give the BBS all of your machines original memory,  
         minus 5K.

         Phoenix           Technical Reference Manual        Page  76

         The advantages are three fold:

         If  you are using a DISK CACHE, it makes the cache that  more  
         effective  by not disturbing the information it  has  already  
         cached.

         You don't have to mess with errorlevels and batch files.

         And finally your matrix messages, events, and routing doesn't  
         have to be redone.

         If  you  use  the SHELL method, Phoenix will  LOG  the  SHELL  
         command  line to your Phoenix.log and to the display  screen.  
         This  can be useful if you need to debug your  SHELL  Command  
         line.

         If  for  some reason no application was executed  during  the  
         SHELL,  Phoenix calls it a SPAWN, that information will  also  
         be displayed on the screen and added to the Phoenix.log.

         The second method is EXITING with ERRORLEVEL 255. Although  I  
         can  see  no reason WHY you would HAVE or WANT  to  use  this  
         method, it is available.
 
         When  a Human calls, Phoenix will create a batch file  called  
         RUNBBSn.BAT file, n is  the  serial  port you're on. 

         If  you're  using  COM 2, the  name  of  the  file  would  be  
         RUNBBS2.BAT and the contents of the RUNBBS2.BAT  file: 

         HUMAN2 <Connect Rate> <Serial Port #> <Time To Next Event>  

         (It is up to YOU to create HUMAN2.BAT. This is the BATCH file  
         that ACTUAL calls the BBS).

         After   creating  RUNBBS2.BAT,  Phoenix  will    exit    with   
         errorlevel  255. It is up to you to trap that errorlevel  and  
         call  RUNBBS2.BAT file. RUNBBS2.BAT will,   in   turn,   call  
         HUMAN2.BAT which is your actual CBIS batch file. 

         Keep  in mind the 2 is ONLY used if you are using COM  2.  If  
         you  are  using  COM  1 then  it  would  be  RUNBBS1.BAT  and  
         HUMAN1.BAT.
                               Smart(tm) Packer

         Phoenix  has  its  own internal packing  system  that  places  
         messages  in  PKT format. You don't need an  external  packer  
         like OMMM or PACKER.EXE.

         The  internal  packer  is a SMART packer.  It  can  tell  the  
         difference  between  a FILE REQUEST, a  SERVICE  REQUEST,  an  
         ECHOMAIL BUNDLE, and a regular FILE.


         Phoenix           Technical Reference Manual        Page  77

         With  a  regular  file  you would want to  send  the  message  
         header  so the other system can, if it's an ISIS  or  Phoenix  
         mailer,  automatically  ROUTE  the  file  on  to  its   final  
         destination.

         But with the FREQ, SRV, and ECHO messages the message  header  
         would just clutter up the other systems matrix area.

         The SMART packer will SKIP those messages when it packs for a  
         particular  system.  If NO message headers  were  packed,  no  
         matrix  mail or regular file attaches, the SMART packer  will  
         create a NULL PACKET. 

         A NULL Packet is a 58 byte PACKET HEADER with no messages. It  
         gives  the receiver a way of figuring out WHO is calling,  if  
         the receiver uses that method (Binkley does even if you do  a  
         WAZOO  session.)  without  cluttering his  matrix  area  with  
         useless messages. 

         The  SMART  packer will ignore any file request  and  service  
         requests if they are for a system that is calling YOU.

         The  SMART packer doesn't PREPACK the messages. Messages  are  
         only PACKED into PKT format when Phoenix needs to actual SEND  
         them.

         The only time messages are PREPACK is right before placing an  
         outbound  call. Since it has to SEARCH to see if anything  is  
         going  out,  it  creates  a TEMPORARY PKT  as  it  finds  the  
         messages.  It is something that would have to be done  anyway  
         and this does away with a little redundant processing. 

         What  happens  if a message has been routed  to  a  different  
         domain address and the system it was originally FOR calls?

         E.g.  Messages for 1.237.504.0 were routed to  1.237.0.0  and  
         1.237.504.0 calls with a file request.

         Phoenix  would give him his messages. It KNOWS who they  were  
         originally for and will simply route them BACK to him.


                        Maximum Number Of Outbound Messages

              The  maximum  number of outbound  messages  Phoenix  can  
              handle at once is 256. 

              This  limit  can be raised if the need arises,  but  256  
              seems  like  plenty.  





         Phoenix           Technical Reference Manual        Page  78

                                  Phoenix.sav

         Phoenix  creates  a  file in your  current  directory  called  
         "PHOENIX.SAV".

         This  file  contains  a complete TEXT copy of  ALL  inbound  and  
         outbound MATRIX messages, in ASCII format.

         The  ARRIVAL  time  is  the  date  the  message  ARRIVED   or  
         ORIGINATED in your matrix area.

         This allows you to go back and retrieve messages you may have  
         sent  days,  weeks, or even months before, in case  you  need  
         to reference or resend one.

                               Alternate Domains

         It  is  common  practice among Fidonet sysops  to  belong  to  
         multiple  networks or even have multiple domains  within  the  
         same network.

         You can define up to 53 ALTERNATE DOMAIN ADDRESSES, 3 in  the  
         Phoenix  configuation  file and 50 in an external  text  file  
         called phoenix.aka. 
 
         Phoenix NEEDS to know about the alternate domains to  prevent  
         it  from PACKING mail to YOUR OWN ADDRESS. Although it  would  
         never  be sent, it takes up space in the packet table and  it  
         takes  time to load and attempt to ROUTE. The implied  router  
         needs  to know ALL of your address so it can  properly  route  
         mail.

         If  a  mailer calls and their ZONE is one of  YOUR  alternate  
         Domain  ZONE's, Phoenix will switch to the  ALTERNATE  domain  
         address for that ZONE and your HMS or WAZOO header will  show  
         the  ALTERNATE domain address instead of the  default  DOMAIN  
         address.

         If Phoenix has to pack any messages for the calling system to  
         PICKUP, the packet HEADER (not the messages themselves,  they  
         are  not  touched) will show your  HIGHEST  ALTERNATE  domain  
         address within that ZONE and NET or highest alternate address  
         within that ZONE as the PACKING system. 

                                    Phoenix.aka

              Phoenix.aka  is an optional text file, located  in   the  
              phoenix directory.

              Each  line contains one domain address and you can  list  
              up   to 50  alternate  addresses, that should be  enough   
              for  anyone.


         Phoenix           Technical Reference Manual        Page  79

              An example of a Phoenix.aka file:

              1.296.5.0
              500.500.1.0
              500.214.0.0
                   
               How To Pickup Mail When Multiple Domains Are Involved
              
              The first method would be used if you pickup mail  going  
              to more than one network domain at a single location.

              Assuming  you  were  the ECHOMAIL gate  to  Fidonet  and  
              Family.  Your Fidonet domain might be 1.237.504.0,  your  
              Family  Net domain might be 10.200.10.0 and your  TCP/PC  
              domain would be 99.234.1.0 and your feed for Fidonet and  
              FamilyNet  is the same PHYSICAL system and  his  primary  
              Fidonet address is 1.134.500.0. (THAT is a mouth full!)

              1.134.500.0   also   has  the   FamilyNet   address   of  
              10.100.9.0.

              You  would  have  1.134.500.0 route ALL  mail  going  to  
              1.237.504.0 AND 10.200.10.0 to 99.234.1.0, your  primary  
              DOMAIN address. And, you would route all 10.100.9.0  and  
              1.134.500.0 mail to 1.134.500.0

              When  you  call  1.134.500.0 using  your  TCP/PC  domain  
              (99.234.1.0),  you  would  be able to pick-up  all  mail  
              original  addressed  to  1.237.504.0,  99.234.1.0,   and  
              10.200.10.0.  That would include any  echomail  bundles,  
              file attaches, and standard MATRIX mail.

              Because this is all done PRIOR to the physically connect  
              between  the  two systems, it is very  DATA  secure  and  
              fast.

              Some  mailers have rather limited  routing  capabilities  
              and  cannot handle routing echomail and  file  attaches.  
              Avoid doing mail with those system if multiple  networks  
              are  involved unless it is a local call. If  you  cannot  
              avoid  doing mail with them and they support  EMSI  then  
              you  have no other option but to use EMSI when you  call  
              THEM.
              
              Picking  up  when only ONE ALTERNATE domain  address  is  
              involved:

              Phoenix  will  switch to the  ALTERNATE  Domain  Address  
              prior to placing the call. 
         




         Phoenix           Technical Reference Manual        Page  80

              Lets   assume  you  defined  an  ALTERNATE   DOMAIN   of  
              1.237.504.0  and 1.100.10.0 is the system in  the  other  
              DOMAIN. You primary domain is 99.99.1.0.

              Prior  to PLACING the call, Phoenix will  simply  switch  
              your  primary domain address to 1.237.504.0.  After  the  
              call,  Phoenix will switch your PRIMARY  domain  address  
              BACK to 99.99.1.0.

              You  can override this with the Explicit Route Noun  USE  
              ADDRESS x.x.x.x For X.X.X.X


                                Busy The Modem

         Phoenix  will  BUSY  the  modem  when  it  does  any  of  the  
         following. 

         1. Scans the matrix area for mail.
         2. Performs IMPLIED routing.
         3. Reads and executes any EXPLICIT routing instructions.
         4. Executes any EVENT batch file.
         5. Exits with an errorlevel.
         6. Unbundles matrix mail.
         7. Executes ECHOMAIL.BAT.

                      Auto Detecting Osiris Bbs Software

         When Phoenix loads it does a QUICK search for the ENVIRONMENT  
         variable   "OSIRIS=".   If  it  finds   that   variable,   it  
         automatically  engages  the SHELL to BBS  using  the  default  
         command  line  "OSIRIS  -B*B -P*P -N*N -T*T".  It  will  also  
         change INTO the Osiris directory before calling the BBS.

         While  this default SHELL command line will be enough for  99  
         percent of the Osiris sysops, some of you may need or want to  
         tailor the command line.

         To tailor the command line use the Config.exe field
         labeled SHELL INSTRUCTIONS.

         Example

         SHELL INSTRUCTIONS OSIRIS -B*B -P*P -N2 -T*T -E: -S384 -O384

         If  you  define shell instructions,  your  instructions  will  
         supersede "OSIRIS -B*B -P*P -N*N -T*T".







         Phoenix           Technical Reference Manual        Page  81

                                Disabling The Shell

              If  for some reason you don't want Phoenix to  SHELL  to  
              Osiris,  define  the following environment  variable  in  
              your AUTOEXEC.BAT:

              NOSHELL=YES

              Phoenix  will  NOT  use  the  SHELL  option  when   this  
              environment variable is present.

                              Testing Your Setup

         When  you  first install Phoenix or rather your  events,  you  
         will need a quick and easy way to TEST exit with a errorlevel  
         (and  how you BATCH file executes that errorlevel) or if  you  
         elect to use the event BATCH file you'll need to test that.

         Since  Phoenix will only exit with the errorlevel or  execute  
         the  event batch file once, you certainly don't want to  wait  
         a day at a time to test any modifications.

         While  Phoenix  is  running, press ALT-Z (Z  for  ZAP).  This  
         wipes  out all information pertaining to which event was  run  
         and  when.  This is basically what happens when  your  system  
         clock goes from 23.59 to 00.00 each night.

         This can also be used to test modifications to a custom route  
         control file.

         Keep  in  mind  that Phoenix will NOT  execute  events  who's  
         ENDING  time  has already passed so you can  only  test  your  
         setup on the CURRENT event. To test events that have  already  
         passed  or  events that are yet to come, change  your  system  
         TIME so that event will be active.

                                   Aborting

         You  can  abort ALMOST everything by pressing  ESC.  

         In  a few places, where TIMING is critical, the  keyboard  is  
         not checked and pressing ESC will have no effect. 

         In  a few places where TIMING is NOT critical but  where  ESC  
         might leave the other system HANGING with its mouth open, ESC  
         will be buffered until it can be safely processed.

                                      Tic

         TIC is a method of automatically ECHOING files from system to  
         system the same way you would echo messages.



         Phoenix           Technical Reference Manual        Page  82


         We  produce a TIC compatible processor called OTC that  works  
         with Phoenix and our BBS program, Osiris.

         The  TIC processor you use would depend on the  BBS  software  
         you're using. 

         If  Phoenix  detects  a TIC control file, they  have  a  file  
         extension  of  .TIC,  it will execute  a  BATCH  file  called  
         "TIC.BAT"

         You  can place any TIC processing instructions in this  batch  
         file.
                                     Raid

         Raid  is  a TIC utility that allows remote  systems  to  ADD,  
         REMOVE, or get a list of the TIC areas they have access to.

         When  Phoenix  scans  the matrix area,  building  the  matrix  
         tables,  and it DETECTS a message addressed to RAID, it  will  
         call the batch file "RAID.BAT".

         You  should place any PROCESSING instructions for  YOUR  raid  
         program in this file.

         If your RAID utility is actual named "RAID.EXE or  RAID.COM",  
         you  will need to RENAME it to keep it from conflicting  with  
         the RAID.BAT file.

                                    Areafix

         Areafix is a program that allows systems picking up  echomail  
         from  you  to automate the process of  adding,  removing,  or  
         getting lists of their areas and available areas.

         When  Phoenix  scans  the matrix area,  building  the  matrix  
         tables,  and  it DETECTS a message addressed to  AREAFIX,  it  
         will call the batch file "AFIX.BAT".

         You should place any PROCESSING instructions for YOUR areafix  
         program in this file. 
                     Afix.bat, Tic.bat, Raid.bat, Echomail.bat

              Ok,  no  one builds TIC and RAID into  their  mailer  so  
              we're  one  up. But, several mailers build  Areafix  and  
              Echomail  programs directly into the mailer, why  do  we  
              call batch files? 

              While that can be 'NICE', it is a rather limited feature  
              because  not all BBS' use the same type of message  base  
              structures or the same type of ECHO control files.



         Phoenix           Technical Reference Manual        Page  83


              This method doesn't FORCE you to use any particular type  
              of  BBS  and lets YOU pick the Echomail, TIC,  RAID,  or  
              AREAfix programs that YOU like.

                             Master Transfer Timer

         During  Field  Tests, we found something we have  never  seen  
         before. While transferring a 360K file to a D'bridge  system,  
         the D'bridge system allowed the entire file to be transferred  
         and  when  End of file was sent, the D'bridge system  sent  a  
         ZRPOS 0, meaning error resend from position 0. Position 0  is  
         the  BEGINNING of the file. 

         While   this  would  be  considered  to  be   very   strange,  
         considering  that it takes about 4 minutes to send  the  file  
         (v32bis),   we  didn't think a WHOLE lot about it  until  the  
         same  thing happened when the end of file was again  reached.  
         Phoenix resent the file for the 3rd time and when end of file  
         was  again reached, for the 3rd time, D'bridge did  the  same  
         thing.

         We  don't know HOW long this would have continued (we  manual  
         killed  the  transfer)  but  in  THEORY,  it  could  continue  
         forever.  Since  50 percent of the file was sent  without  an  
         error, Phoenix would reset the error counter back to zero.

         To prevent something like that from ever happening again,  we  
         installed a MASTER transfer timer. When Phoenix estimates the  
         transfer  time for the file, a master timer is set  to  three  
         times  the  estimated transfer time. 

         In  other words, if the estimated transfer time is 4  minutes  
         and 20 seconds, the master timer would be set to  780 seconds  
         (  13  minutes).  If the file hasn't been  sent  OR  received  
         BEFORE this timer expires, carrier will be dropped.

         The MINIMUM is 120 seconds, 2 minutes. If the master transfer  
         time  comes  up  less  than 120 seconds, it  is  set  TO  120  
         seconds. This should give PKT's, REQ's, and other small files  
         plenty of time.
                              Msg Storage Format

         We're  use  the following structure for .MSG as  outlined  in  
         Fidonet  Technical Standards document  FTS-0001.015,  version  
         015. 

         NOTE:  Stored format should NOT be confused with  the  format  
         used  between  mailers  during  a  mail  session,  they   ARE  
         different.




         Phoenix           Technical Reference Manual        Page  84

         1.  Application  Layer  Data Definition :  Stored Message


       Offset
      dec hex
              .-----------------------------------------------.
        0   0 |                                               |
              ~                 fromUserName                  ~
              |                   36 bytes                    |
              +-----------------------+-----------------------+
       36  24 |                                               |
              ~                  toUserName                   ~
              |                   36 bytes                    |
              +-----------------------+-----------------------+
       72  48 |                                               |
              ~                    subject                    ~
              |                   72  bytes                   |
              +-----------------------+-----------------------+
      144  90 |                                               |
|             ~                    DateTime                   ~
              |                    20 bytes                   |
              +-----------------------+-----------------------+
      164  A4 | timesRead (low order) | timesRead (high order)|
              +-----------------------+-----------------------+
      166  A6 | destNode (low order)  | destNode (high order) |
              +-----------------------+-----------------------+
      168  A8 | origNode (low order)  | origNode (high order) |
              +-----------------------+-----------------------+
      170  AA |   cost (low order)    |   cost (high order)   |
              +-----------------------+-----------------------+
      172  AC | origNet (low order)   | origNet (high order)  |
              +-----------------------+-----------------------+
      174  AE | destNet (low order)   | destNet (high order)  |
              +-----------------------+-----------------------+
|     176  B0 | destZone              | destZone              |
|             +-----------------------+-----------------------+
|     178  B2 | origZone              | origZone              |
|             +-----------------------+-----------------------+
|     180  B4 | destPoint             | destPoint             |
|             +-----------------------+-----------------------+
|     182  B6 | origPoint             | origPoint             |
              +-----------------------+-----------------------+
      184  B8 | Attribute2(low order) | Attribute2 (highorder)|
              +-----------------------+-----------------------+
      186  BA | Attribute (low order) | Attribute (high order)|
              +-----------------------+-----------------------+
      188  BC | Msg Type  (low order) | Msg Type  (high order)|
              +-----------------------+-----------------------+
      190  BE |                      text                     |
              ~                    unbounded                  ~
              |                 null terminated               |
              `-----------------------------------------------'


         Phoenix           Technical Reference Manual        Page  85

         *NUMBER*  indicates this bit flag is used for something  else  
         other  than  what  it was orginally used  for.  None  of  the  
         modifications  to the  bit flags will effect most  3rd  party  
         applications that supports the Fidonet .MSG format. 


      AttributeWord   bit       meaning
                      ---       --------------------
           *1*          0       Private
                        1       Crash
                        2       Recd
           *2*          3       Sent        
                        4       FileAttached
                        5       Unused
                        6       Orphan
           *3*          7       Kill Sent,Only Use If A File Attach.
                        8       Local
                        9       HoldForPickup
           *4*         10       Reserved By Phoenix
                       11       Unused                       
                       12       Unused                       
           *5*         13       No Send Msg Header
                       14       Unused       
                       15       Unused


         *1*  : Not needed, Phoenix considers ALL mail as Private  and  
                automatically  sets  the PRIVATE flag  on  all  matrix  
                messages sent FROM your system.
         *2*  :Not Used because Phoenix automatically deletes the  MSG  
               after is has been sent.  
         *3* : Originally Kill message. However, Phoenix automatically
               deletes  messages after they are sent. We use  this  to  
               tell  Phoenix to DELETE the file attach, after  it  has  
               been sent.
         *4* : Originally defined as UNUSED so Phoenix reserves it for
               internal use.
         *5*  : Original used to flag a message as a  RETURN  receipt  
                reply. However, this is not needed by Phoenix  because  
                a return receipt reply is just a plan message. We  use  
                it  to flag messages so that only the file  attach  is  
                sent, the body and message header is not sent. 

         The nextReply and replyTo fields are reserved for the Message  
         Editor  to  use  for reply  linking.  Since  Phoenix  deletes  
         messages  once they are sent, there would be nothing to  LINK  
         so we use the two fields for something else.

         Msg TYPE use to be the nextReply field in the message header.  
         It   is now uses as a TYPE bit flag field to quickly  ID  the  
         TYPE of message. 



         Phoenix           Technical Reference Manual        Page  86

         The following attributes are used.

         Bit           Meaning
         ----------------------------------
         0             Unused
         1             Plain File Attach. 
         2             File Request.
         3             Echomail Bundle
         4             Service Request
         5             Tic


         Phoenix  can  auto-detect the following TYPES if the  ID  bit  
         flag  is  not supported by the application that  created  the  
         message.

         Echomail Attaches.
         TIC. 
         Service Requests.
         File Requests.

         It is considerably faster to use the ID bit flags.

         The Attribute2 field use to be the ReplyTo field. It is  used  
         as a secondary ATTRIBUTE bit flag field. Right now only 1 bit  
         flag  uses this field, 0x0001. This indicates the message  is  
         to  go  DIRECT  passing  any  type  of  routing,  Implied  or  
         Explicit.

         None  of the modifications to the .MSG structure will  effect  
         most  3rd party applications that supports the  Fidonet  .MSG  
         format. 

         The  zone  and  point fields, origin  and  destination,  were  
         originally  defined  as OPTIONAL. They are  not  optional  in  
         Phoenix because Phoenix uses all four subdomains.

         If the application that created the message does not  support  
         zones,  it  must zero those fields.  Most  programmers,  good  
         ones, will automatically zero a file structure prior to using  
         it  so you should never see wild zone numbers. 

         If Phoenix finds any ZONE 0 fields, it will scan the body  of  
         the  message to see if there is an INTL line. If so, it  will  
         pull  the  Zone addresses from the body of  the  message  and  
         REWRITE  the  message  header  to  include  the  proper  zone  
         addresses.  If  there  is NO INTL line and  the  zone  is  0,  
         Phoenix  will  ASSUME  the  zone is  equal  to  your  primary  
         address.

         While they are not need by Phoenix, it also supports some  of  
         the  kludge  line ^AFLAGS used by  Frontdoor,  D'bridge,  and  
         several other mailers.

         Phoenix           Technical Reference Manual        Page  87

         ^AFLAGS supported are: IMM, KFA, and DIR

         IMM  will be remapped to the CRASH ATTRIBUTE.

         KFA will be remapped to the KILL ATTRIBUTE.

         DIR will be remapped to the DIRECT ATTRIBUTE.

         Phoenix  only  needs  to do this once.  If  Phoenix  finds  a  
         ^AFLAGS  in a message, the message header attribute and  type  
         flag  fields  are updated and the message header  is  written  
         back  to disk. This saves a CONSIDERABLE amount of  redundant  
         processing  and why we don't use the ^AFLAGS approach in  our  
         applications.

                               Security Systems

         Phoenix  has  a MULTIPLE level security system  for  business  
         that need the ULTIMATE in data security.

         Just how much security you want or need is up to you.

                                  Secure  Address

              If any outbound call is placed and the answering  system  
              doesn't pass the address Phoenix used to PLACE the call,  
              Phoenix  hangs up figuring the phone company  goofed  or  
              YOU goofed. If any system CALLS IN, they MUST be  listed  
              in your nodelist or Phoenix hangs up.

























         Phoenix           Technical Reference Manual        Page  88

                              Session  Level  Password

              If  the  CALLING  system does NOT  provide  the  correct  
              SESSION  password, the one YOU defined in  the  nodelist  
              record for THAT system, Phoenix hangs up. 

                              System  Level  Password

              ALT-C  into CONFIG and click on the MORE box.  When  the  
              MORE  screen opens, you'll see two fields  labeled  "HMS  
              ONLY"  and "SYSTEM PASSWORD". You can enter up to  a  10  
              digit  numeric password ( over 2 billion combinations  )  
              that  ALL systems MUST provide. 

              Since ONLY HMS sessions provide support for SYSTEM level  
              passwords,  you should, not required, toggle "HMS  ONLY"  
              to YES to prevent OTHER types of mail sessions.

              If  you  are CALLING a system that HAS  a  system  level  
              password, you'll find a field in the nodelist record for  
              THAT system's system level password.

                            Require Pwd For Mail Pickup

              This  augments the SESSION passwords by  REQUIRING  some  
              type  of session level password in order for mail to  be  
              picked  up.  This doesn't CHECK the  password,  it  only  
              requires that one be passed. 

              Case  in point, you are a RC and you route all  mail  to  
              the  HOST/HUB systems and they send it on to  its  final  
              destination. Suppose you have mail for 1.200.20.0 and it  
              is   routed  to  1.200.0.0  (normally  would   be)   but  
              1.200.20.0 calls your system with a file request. 

              Under  normal circumstances, Phoenix would give him  his  
              mail. But, someone could be FAKING 1.200.20.0's  address  
              in order to to INTERCEPT his mail. 

              1.200.20.0  DOES use a session level password  with  his  
              host,  1.200.0.0,  and SO do you. BUT . . . you  do  NOT  
              have  a  session level password  set-up  for  1.200.20.0  
              because you don't do mail directly with him.

              If  you  toggle "Require Pwd For Mail  Pickup"  to  yes,  
              Phoenix would NOT give him his mail because no passwords  
              were  INVOLVED. His FILE REQUEST would be  accepted  and  
              processed.


         Phoenix  has several internal security systems that  function  
         automatically  to prevent "SLICK WILLYS". We'll not get  into  
         what a SLICK WILLY is, but it can be a bitch.

         Phoenix           Technical Reference Manual        Page  89

                                   Port.dat

         Phoenix  gets  information about your SERIAL  port  from  the  
         PORT.DAT file. 

         This file contains information about the BASE address and IRQ  
         Mask.

         You  should be VERY careful  about changing ANYTHING in  this  
         file.

         To edit or view PORT.DAT, run CONFIG.EXE and move your  mouse  
         cursor to the BOX labeled "COM IRQS" and click the left mouse  
         button.

         To  change a field, move the mouse cursor to that  field  and  
         click the LEFT mouse button and then enter the new data.  You  
         MUST enter the data in BASE 16.

         To  SAVE  your changes, move to the BOX  labeled  "SAVE"  and  
         click the LEFT mouse button. Clicking on CANCEL will take you  
         back  to the main screen without saving any changes  you  may  
         have made.































         Phoenix           Technical Reference Manual        Page  90

                      Serial Drivers And Multi-Port Cards

         Phoenix supports for Intelligent multi-port  serial  cards,  
         non-intelligent multi-port serial cards, fossils, and has  an  
         internal  serial driver (fastest method of dealing  with  the  
         serial port).

         Phoenix defaults to the  internal high speed driver, but  you  
         can  change the driver type by using the use the  environment  
         variable COMDRV.
 
         COMDRV=FOSSIL
 
         {Intelligent Serial Cards}
 
         COMDRV=STARGATE 
         COMDRV=DIGI 
         COMDRV=ARNET
 
         {Non-Intelligent Serial Cards}
 
         COMDRV=NDIGI 
         COMDRV=NSTARGATE 
         COMDRV=AST 
         COMDRV=BOCA

 
                          Intelligent Multi-Port Stargate
 
              Load  the  Star  Gate device driver,  ACL.SYS,  in  your  
              config.sys.  When  your  system  boots,  run  ACLDL   to  
              download your code.
 
              Phoenix defaults to the 16 port with the I/O address  of  
              0x200  at D000:000 starting at COM 5. If  your  hardware  
              doesn't  match this, you'll need to create a  SERIAL.CFG  
              control  file in your current directory  or  reconfigure  
              your stargate board.
 
              SERIAL.CFG for STARGATE Intelligent Multi-port Cards:
 
              The  first line of this file should contain 5  settings,  
              separated by a single space.
 
              BOARD BOARD_SEGMENT PORT FIRST_PORT_NUMBER NUMBER_OF_PORTS
 
              Board: Stargate board to use (0 - 3). Phoenix/Osiris can  
              handle  up to four stargate boards ( 64 ports) at  once.  
              This tells us which board you want to use.
 
              Board_segment:  Segment of the Star Gate board's  memory  
              window.
 

         Phoenix           Technical Reference Manual        Page  91

              Port: The Address of the board's I/O latch.
 
              First_port_number:  Name given to the first port on  the  
              board  (1,2,3,etc). The designation of the  port  number  
              for the first port on the board is arbitrary.
 
              Number_of_ports: Number of ports on the board.
 
              Example:
 
              {SERIAL.CFG}
 
              0 0xd000 0x300 4 8
 
                            Intelligent Multi-Port Arnet
 
              When  you  load  the Arnet device  driver,  port  number  
              assignments  are printed on the display. These  are  the  
              number you'd use in the Phoenix PORT field (Config.exe).
 
              Use  the /N5 switch on ASP.SYS. If you do not  use  this  
              switch,  attempts to set handshaking will result  in  an  
              error.
 
              The  files, box.bin and fastbios.bin, supplied with  the  
              Arnet boards, must be in your root directory for this to  
              work  properly. These files are used by ASP.SYS at  boot  
              time.
 
                          Intelligent Multi-Port Digiboard
 
              Run  the Digiboard config. program (XIDOSCFG.EXE)  which  
              asks you for the desired port numbers. Also, install the  
              device  driver  supplied with the board. You  must  also  
              complete the following steps:
 
              1. Set up the board NOT to use interrupts.
 
              2. Setup to support INT 0x14 for most drivers and  EBIOS  
              for the XIDOS5 driver.
 
              3.  Change  the configuration to enable ports,  if  your  
              driver  requires  it. Make sure "NONE" is  the  selected  
              handshaking for ports.
 
              4.  Reboot  your  system. During the  boot,  the  driver  
              should   respond   with   the   message    "successfully  
              initialized board".
 





         Phoenix           Technical Reference Manual        Page  92

                                       Fossil
 
               Any  fossil  driver will work. See  documentation  that  
              comes with the fossil driver for details.
 
                            Non-Intelligent Serial Cards
 
              Non-Intelligent  boards  frequently  come  with   device  
              driver  software. This software provides INT 14H  access  
              to  the  UART on the board. Do N O T use  this  software  
              with   Phoenix/Osiris.   PHoenix/Osiris   accesses   the  
              hardware  directly  without  the  use  of  any  external  
              drivers.

                             Non-Intelligent Digiboards 
                                   (COMDRV=NDIGI)
 
              The  Digiboard  DigiCHANNEL PC/16, PC/8,  and  PC/4  are  
              multi-channel  communications  boards  that  provide   a  
              serial  communications  subset for  IBM  and  compatible  
              computers.  Each  of  the  boards  supports  full  modem  
              control  on  each port. Up to two DigiCHANNEL  PC/16,  4  
              PC/4  or  PC/8  boards  can be  installed  on  a  single  
              computer providing up to 32 additional ports.
 
              To   insure  connection  flexibility,  3   options   are  
              available:
 
              1. An I/O mate connection box with external connections.
 
              2. An octopus cable with four or eight DB25 connectors.
 
              3.  An  RJ45  connection box with  eight  RJ45  or  RJ11  
              connectors.
 
              The   DIGI  PC/4  and  PC/8  addressing  and   interrupt  
              selection  are flexibly and not limited to preset  IRQs,  
              address,  or  address  ranges.  The  user  may  set  DIP  
              switches to select different status registers (DS1)  and  
              I/O  port  addresses  (DS2 - DS9), as  well  as  setting  
              jumpers to select either one or two interrupts.
 
              The DIGI PC/16 offers hardware jumpers for selecting  an  
              interrupt  and  a PAL with preset I/O  port  and  status  
              register addresses.
 
              There  are  six possible system interrupts that  may  be  
              selected for the DIGI PC/X board: IRQ2 - IRQ7.  However,  
              IRQ3  and IRQ4 are commonly reserved for  standard  COM1  
              and COM2 serial hardware.
 



         Phoenix           Technical Reference Manual        Page  93

              If  multiple  boards are installed in one  system,  each  
              board is given a unique I.D. such as board 0 and board 1  
              by setting the board ID jumpers. The status register and  
              IRQ  of  ALL boards can be set to the same  values,  and  
              the  boards are daisy changed with special  cables  that  
              pass  signals from the interrupt sequencer.  When  daisy  
              chained,  the  boards are treated like  one  board.  The  
              boards  can  also be setup  independently  on  different  
              interrupts.
 
                            Setting Up  The Digi Pc/4 Board 

                   The  COM/4  board  has 4  serial  interface  ports,  
                   individual address and interrupt settings, and  two  
                   8 bit status ports. It is preset and tested at  the  
                   factory  at IRQ3; address 100, 108, 110,  and  118;  
                   status port ON, and set to address 140. Check  your  
                   system for any peripherals that may use either  the  
                   preset  interrupt  or  addresses. If  there  is  no  
                   conflict,  you can install the COM/4 board  without  
                   modifications.  However,  if  you  need  to  change  
                   settings, details are provided below.

 
                                     Setting The Jumpers
 
                        Jumpers  1-4 are used to choose the  interrupt  
                        for each individual port.
 
                        For odd interrupts IRQ3, IRQ5, or IRQ7 set the  
                        shunt   between   pins  1  and   2   for   the  
                        corresponding jumper.
 
                        For  even interrupts IRQ2, IRQ4, or  IRQ6  set  
                        the  shunt  between  pins  2  and  3  for  the  
                        corresponding  jumper. Ports 1 through  4  map  
                        with jumpers 1-4 respectively.
 
                        J9  and  J10  are used to  set  the  board  ID  
                        number.  The  setting will depend  upon  which  
                        board  it represents. If more than  one  board   
                        is used in the system, each board must be  set  
                        to  a unique identification number. The  first  
                        board  should always be set to 0. If you  have  
                        daisy  changed more than one  board, you  will  
                        use  the  board #s 1-3. The  settings  are  as  
                        follows:
 






         Phoenix           Technical Reference Manual        Page  94

  Board #            J9                       J10 
  ------------------------------------------------------------ 
    0        between pins 2 and 3     between pins 1 and 2 
    1        between pins 2 and 3     between pins 1 and 2 
    2        between pins 1 and 2     between pins 2 and 3 
    3        between pins 1 and 2     between pins 1 and 2
 
                        J85  through  J90  are used  to  select  which  
                        interrupt  the  board  will  use.  Set   these  
                        jumpers as follows:
 
                         IRQ#               Jumper# 
                         --------------------------- 
                         2                  J90 
                         3                  J85 
                         4                  J89 
                         5                  J86 
                         6                  J88 
                         7                  J87
 
                                    Multi-Board Connectors
 
                        P2 and P3 are jumpers used to daisy chain  two  
                        boards  together  using  a  special  DigiBoard  
                        cable. If you are only using one board,  place  
                        a  shunt  on  pins 2 and 3 of  both  of  these  
                        jumpers. This is VERY important. Without  this  
                        shunt, no interrupts will be received.
 
                                         Dip Switches
 
                        Address line A3 through A9 determine the  port  
                        address  and  are logic-selected  on  the  DIP  
                        switches  for  each  port  for  switches   DS3  
                        through  DS5. The DIP switches for  each  port  
                        can  be set to any NON-CONFLICTING address  in  
                        the I/O map from 0000H to 03FFH.
 
                        Switch positions 1-7 switch set the address of  
                        each port. Position 1 corresponds to A9, 2=A8,  
                        3=A7,  4=A6, 5=A5, 6=A4, 7=A3. Position  8  of  
                        each  switch enables or disables the port.  We  
                        recommend  assigning consecutive port  numbers  
                        for easy of use.
 
                        The  following table lists  suggested  address  
                        and   switch   settings  for   the   DigiBoard  
                        DigiCHANNEL PC/4 board:






         Phoenix           Technical Reference Manual        Page  95

 
   Port#   Base    Dip                  Switch Settings 
           Address Switch   1    2    3    4    5    6    7    8 
   ---------------------------------------------------------------- 
    Status 140H    DS1      ON   OFF  ON   OFF  ON   ON   ON   ON 
    port 
   ---------------------------------------------------------------- 
     1     100H    DS2      ON   OFF  ON   ON   ON   ON   ON   ON 
     2     108H    DS3      ON   OFF  ON   ON   ON   ON   OFF  ON 
     3     110H    DS4      ON   OFF  ON   ON   ON   OFF  ON   ON 
     4     118H    DS5      ON   OFF  ON   ON   ON   OFF  OFF  ON

                        Position   (Switch  setting  8)   enables   or  
                        disables the port where ON = enabled.

 
                              Setting Up A Digiboard Pc/8 

                   The   PC/8  board  has  eight   individual   ports,  
                   individual address and interrupt settings and two 8  
                   bit status ports.
 
                   The PC/8 board is preset and tested at the  factory  
                   using  IRQ3; address 100, 108,110, 118,  120,  128,  
                   130,  and  138; status port ON and set  to  address  
                   140.

                                     Setting The Jumpers
 
                        Jumpers J1-J8 are used to choose the interrupt  
                        for  each  port.  For  odd  interrupt  numbers  
                        including  IRQ3, IRQ5, or IRQ7, set the  shunt  
                        between  pin  1 and 2  for  the  corresponding  
                        jumper.
 
                        For  even  interrupts, set the  shunt  between  
                        pins  2 and 3. All ports HAVE to use the  same  
                        interrupt to work properly. Ports 1 through  8  
                        map to jumpers 1-8 respectively.

                        J9  and  J10  are used to  set  the  board  ID  
                        number.  The  setting will depend  upon  which  
                        board  it represents. If more than  one  board   
                        is used in the system, each board must be  set  
                        to  a unique identification number. The  first  
                        board  should always be set to 0. If you  have  
                        daisy  changed more than one  board, you  will  
                        use  the  board #s 1-3. The  settings  are  as  
                        follows:
 




         Phoenix           Technical Reference Manual        Page  96


  Board #            J9                       J10 
  ------------------------------------------------------------ 
    0        between pins 2 and 3     between pins 1 and 2 
    1        between pins 2 and 3     between pins 1 and 2 
    2        between pins 1 and 2     between pins 2 and 3 
    3        between pins 1 and 2     between pins 1 and 2
 
                        J85  through  J90  are used  to  select  which  
                        interrupt  the  board  will  use.  Set   these  
                        jumpers as follows:
 
    IRQ#               Jumper# 
    --------------------------- 
    2                  J90 
    3                  J85 
    4                  J89 
    5                  J86 
    6                  J88 
    7                  J87
 
                                    Multi-Board Connectors
 
                        P2 and P3 are jumpers used to daisy chain  two  
                        boards  together  using  a  special  DigiBoard  
                        cable. If you are only using one board,  place  
                        a  shunt  on  pins 2 and 3 of  both  of  these  
                        jumpers. This is VERY important. Without  this  
                        shunt, no interrupts will be received.
 
                                         Dip Switches

                        Address line A3 through A9 determine the  port  
                        address  and  are logic-selected  on  the  DIP  
                        switches  for  each  port  for  switches   DS3  
                        through  DS5. The DIP switches for  each  port  
                        can  be set to any NON-CONFLICTING address  in  
                        the I/O map from 0000H to 03FFH.
 
                        Switch positions 1-7 switch set the address of  
                        each port. Position 1 corresponds to A9, 2=A8,  
                        3=A7,  4=A6, 5=A5, 6=A4, 7=A3. Position  8  of  
                        each  switch enables or disables the port.  We  
                        recommend  assigning consecutive port  numbers  
                        for easy of use.
 
                        The  following table lists  suggested  address  
                        and   switch   settings  for   the   DigiBoard  
                        DigiCHANNEL PC/8 board:
 




         Phoenix           Technical Reference Manual        Page  97

   Port#   Base    Dip                  Switch Settings 
           Address Switch   1    2    3    4    5    6    7    8 
   ---------------------------------------------------------------- 
    Status 140H    DS1      ON   OFF  ON   OFF  ON   ON   ON   ON 
    port 
   ---------------------------------------------------------------- 
     1     100H    DS2      ON   OFF  ON   ON   ON   ON   ON   ON 
     2     108H    DS3      ON   OFF  ON   ON   ON   ON   OFF  ON 
     3     110H    DS4      ON   OFF  ON   ON   ON   OFF  ON   ON 
     4     118H    DS5      ON   OFF  ON   ON   ON   OFF  OFF  ON 
     5     120H    DS6      ON   OFF  ON   ON   OFF  ON   ON   ON 
     6     128H    DS7      ON   OFF  ON   ON   OFF  ON   OFF  ON 
     7     130H    DS8      ON   OFF  ON   ON   OFF  OFF  ON   ON 
     8     138H    DS9      ON   OFF  ON   ON   OFF  OFF  OFF  ON
 
                        Position   (Switch  setting  8)   enables   or  
                        disables the port where ON = enabled.

 
                             Setting Up The Digiboard Pc/16 

                   This  board  is, in most respects,  the  functional  
                   equivalent of two DigiChannel PC/8 boards operating  
                   together.  The  PC/16 features the same  method  of  
                   interrupt  sequencing in hardware, sparing the  CPU  
                   from having to POLL the individual ports. While the  
                   PC/8  has several DIP switches and jumpers to  set,  
                   the PC/16 has all addresses set in the hardware.
 
                   Default values are set at IRQ3, UART base address =  
                   100h, and status register = 140H.
 
                   To install the board, set the jumpers including the  
                   board  selection  jumper  and  the  IRQ   selection  
                   jumper.
 
                   Check other peripherals for conflicts with the pre- 
                   set addresses. If a conflict occurs, you will  HAVE  
                   to change the I/O port on the OTHER device.
 
                   Connector  Jumper  P3 is used to  daisy  chain  two  
                   boards together using a special Digiboard cable. If  
                   you are only using one board, place a shunt on this  
                   jumper.  It  is located  in  the  upper  right-hand  
                   corner of the board.

                   Interrupt  Jumper J1 through J6 are used to  select  
                   which interrupt the board will use. Set the jumpers  
                   as follows
 




         Phoenix           Technical Reference Manual        Page  98

                    IRQ#           Set the shunt at Jumper # 
                    ---------------------------------------- 
                    2                       J1 
                    3                       J2 
                    4                       J3 
                    5                       J4 
                    6                       J5 
                    7                       J6

 
                   Set the BOARD I.D. Jumper J7 is used to number  the  
                   board if you have more than one cascaded.
 
                   For  Board #0 set the shunt between pins 2  and  3.  
                   For Board #1 set the shunt between pints 1 and 2.

 
              Telling   Phoenix/Osiris   about   the   non-intelligent  
              digiboard board requires you to create a SERIAL.CFG file  
              in the current directory.
 
              The  first  line  of this  file  contains  four  fields,  
              separated by a single space.
 
<IRQ> <Shared_port_status> <First_Port_Number> <Port_Count>
 
              <IRQ> The IRQ line used by this board 3-7.
 
              <Shared_port_status>  Address  of the  status  port  (in  
              HEX).
 
              <First_Port_Number> Number of the first port. This is an  
              arbitrary port number.
 
              <Port_Count> Total number of ports on the board. Be sure  
              to  put the correct total number of ports and  NOT  just  
              the  number of ports you'll be USING. E.g. 4, 8, 16,  or  
              32.
 
              The  Second  line  should contain  the  PORT  ADDRESSES,  
              separated  by a single space, for each port on the  card  
              (In HEX). If you defined Port_Count as 4, then you would  
              have FOUR fields on this line. If you defined port count  
              as 16 then Sixteen fields.

              Example, four port digiboard with default settings using  
              COM5 as the first port number.
 
              {SERIAL.CFG} 

              3 0x140 5 4 
              0x100 0x108 0x110 0x118
 

         Phoenix           Technical Reference Manual        Page  99

                              Non-Intelligent Stargate 
                                 (COMDRV=NSTARGATE)
 
              Telling  Phoenix/Osiris about the  non-intelligent  Star  
              Gate  board requires you to create a SERIAL.CFG file  in  
              the current directory.
 
              Serial.cfg  contains  a  single  line  with  3   fields,  
              separated by a single space.
 
              IRQ FIRST_PORT_NUMBER FIRST_PORT_ADDRESS
 
              IRQ  The IRQ line used by this board (2-7).
 
              FIRST_PORT_NUMBER  Number of the first port. This is  an  
              arbitrary port number.
 
              FIRST_PORT_ADDRESS   Address (In HEX) of the first  UART  
              on the board.
 
              Example:
 
              {SERIAL.CFG}
 
              3 5 0x180
 
                                Non-Intelligent Ast 
                                    (COMDRV=AST)
 
              Telling  Phoenix/Osiris  about the  non-intelligent  AST  
              board  requires you to create a SERIAL.CFG file  in  the  
              current directory.

              Serial.cfg  contains  a  single  line  with  3   fields,  
              separated by a single space.
 
              IRQ FIRST_PORT_NUMBER FIRST_PORT_ADDRESS
 
              IRQ  The IRQ line used by this board (2-7).
 
              FIRST_PORT_NUMBER  Number of the first port. This is  an  
              arbitrary port number.
 
              FIRST_PORT_ADDRESS   Address (In HEX) of the first  UART  
              on the board.
 
              Example:
 
              {SERIAL.CFG}
 
              3 5 0x1a0
 


         Phoenix           Technical Reference Manual        Page 100

                                Non-Intelligent Boca 
                                   (COMDRV=BOCA)
 
              Telling  Phoenix/Osiris about the  non-intelligent  BOCA  
              board  requires you to create a SERIAL.CFG file  in  the  
              current directory.
 
              Serial.cfg  contains  a  single  line  with  4   fields,  
              separated by a single space.
 
              IRQ FIRST_PORT_NUMBER PORT_COUNT FIRST_PORT_ADDRESS
 
              IRQ  The IRQ line used by this board (2-7).
 
              FIRST_PORT_NUMBER  Number of the first port. This is  an  
              arbitrary port number.
 
              PORT_COUNT Total number of ports on the board (4 or 8).
 
              FIRST_PORT_ADDRESS   Address (In HEX) of the first  UART  
              on the board.
 
              Example:
 
              {SERIAL.CFG}
 
              3 5 4 0x180
 
 
                           8259 Interrupt Management
 
         The interrupt manager automatically assigns priority to  each  
         of  the systems interrupts. The timer counter, keyboard,  and  
         cascaded interrupt all have higher priority than the UART.

         To  gain  the  MAXIMUM  throughput  (especially  when  multi- 
         tasking), we suggest that you allow Phoenix to alter the  IRQ  
         manager so the UART has the highest priority.
 
         You can do this using the environment variable 8259=IRQ{1-7}
 
         Examples:
 
         8259=IRQ4 
         8259=IRQ3

         Keep  in  mind that only ONE of the uarts  (in  a  multi-uart  
         environment) can be switched to the HIGHEST priority,  select  
         the one that contains the fastest modem.
 
         NOTE:  Intelligent Multi-port cards use a single shared  IRQ.  
         This is the one you want to give highest priority to.


         Phoenix           Technical Reference Manual        Page 101
          

                      Phoenix Interactive Terminal Module

         The  Terminal module supports the basics such  as  uploading,  
         downloading, data capture, file clipboard, 9 protocols, 16K 8  
         page back scroll buffer with cut file to clipboard, 72  entry  
         dialing directory, rapid fire queue dialing, shell to DOS, an  
         integrated/highly advanced mouse system, and much more.

         The  screen is 24x80 with the 25th line acting as  mini  menu  
         with a clock in the lower right hand corner.

                                   Mouse Commands

              To  open Mouse menu, click RIGHT mouse button.  Move  to  
              the  command  you  want,  they  are  grouped   logically  
              according  to  the function, and click  the  LEFT  mouse  
              button to select. Click the RIGHT mouse button to abort.

              To  CUT  a  file name from the screen,  to  add  to  the  
              clipboard, click the LEFT mouse button. 

              Move  to the first character of the file name and  click  
              the LEFT mouse button to drop the first anchor. Move  to  
              the last character in the file name and click the  RIGHT  
              mouse button.

              A confirmation window will open listing the name of  the  
              file  you  cut from the screen. If you did not  cut  the  
              name  correctly, left off a character or two,  edit  the  
              name  and  press RETURN or CLICK left  mouse  button  to  
              save.

              If  you want to throw the name away, press ESC or  click  
              MIDDLE  mouse  button to clear the name and  then  press  
              RETURN or click left mouse button to exit.

              The MIDDLE mouse button sends a CR/LF to the BBS. Can be  
              used to answer "Press RETURN To Continue" prompts and to  
              select the DEFAULT answer for Y/n, N/y, [C]ontinue etc.

                                       Hotkey

              Each   of the MOUSE menu options can be  activated  with  
              hotkeys. To get help with hotkeys, press ALT-G.


                                 Individual Options

              I'll  not list ALL the options available from the  mouse  
              or  hotkey  menu, some are as plain as the noise  on  MY  
              face :)


         Phoenix           Technical Reference Manual        Page 102

                                        Download

                   This allows you to RECEIVE files from the BBS. When  
                   you select this option, the protocol menu will  pop  
                   open. The cursor will be placed on the protocol you  
                   have set-up as the default protocol for the BBS you  
                   are   currently  connected  to.  To   accept   that  
                   protocol, press RETURN or CLICK left mouse button.

                   If  you  do  not want to use  that  protocol,  move  
                   (arrow  keys  or mouse) to the protocol  you  would  
                   rather  use  and press RETURN or CLICK  left  mouse  
                   button.

                   If  you  select a NON-BATCH protocol, you  will  be  
                   asked to supply the file name.

                                      Upload

                   This  allows you to SEND file(s) to the  BBS.  When  
                   you select this option, the protocol menu will  pop  
                   open. The cursor will be placed on the protocol you  
                   have set-up as the default protocol for the BBS you  
                   are   currently  connected  to.  To   accept   that  
                   protocol, press RETURN or CLICK left mouse button.

                   If  you  do  not want to use  that  protocol,  move  
                   (arrow  keys  or mouse) to the protocol  you  would  
                   rather  use  and press RETURN or CLICK  left  mouse  
                   button.

                   If   you  haven't  set-up  files  in  thee   UPLOAD  
                   CLIPBOARD,  a menu will open. Enter the  name  file  
                   and press ENTER to start the transfer.

                   To  save  connect time, you may want to  enter  the  
                   file  names in the clipboard prior to  calling  the  
                   BBS.

                                        Protocols

                   The  Termainal module has integrated support for  9  
                   of the most popular protocols.

                   Tmodem,  Zmax,  Zmodem,  Ymodem-G,  Ymodem   Batch,  
                   Xmodem-K, Xmodem, HS/Link, and kermit.

                   There is a special REGISTRATION form, REGISTER.FRM,  
                   included for HS/Link. If you feel HS/LINK is  worth  
                   it, you SHOULD do the right thing and register it.




         Phoenix           Technical Reference Manual        Page 103

                   Ymodem-G, don't use it unless you have a 2400  MNP  
                   modem. Without MNP, you aren't likely to finish the  
                   transfer  an  Ymodem-G  can't  restart  an  aborted  
                   transfer.

                   HS/Link is Bi-Directional protocol. That means  you  
                   can send AND receive at the same time. Now you have  
                   no  excuse for NOT uploading files,  especially  to  
                   Osiris  systems which has built in support for  bi- 
                   directional protocols.

                   To  do  a  bi-directional  transfer  with  HS/Link,  
                   select  the Download option on the BBS and type  in  
                   the names of the files you want to download.

                   When  you  select  the  Download  option  and  pick  
                   HS/Link,  it  will  ask  if  you  want  to   UPLOAD  
                   anything.  If  you do, follow  the  procedures  out  
                   lined for uploading.

                   HS/Link is not exceptionally fast so unless you are  
                   going  to  download AND upload files  at  the  same  
                   time,   you  are  better  off  using  a   different  
                   protocol. 

                   You  should ONLY use HS/Link if you  are  connected  
                   at:

                   2400 baud MNP
                   v32 MNP
                   v32bis MNP
                   v32fast MNP
                             
                   Do  NOT  use HS/Link if you connect with  CSP,  HST  
                   14.4,  PEP,  or  HST 16.8. Those  connects  do  not  
                   support bi-directional transfers and your thoughput  
                   will  drop  so  low the  BBS  may  discontinue  the  
                   transfer.  Do  NOT  use HS/Link  without  an  ERROR  
                   correcting connect (MNP or LAP/M).
  
                   Additional  Protocols will be added as  needed.  If  
                   you  find  a  protocol driver  you  feel  is  worth  
                   adding,  send  it to us and if it  proves  to  work  
                   reliably, we will add integrate support for it.

                                   Download Clipboard

                   The Download Clipboard is used to store file  names  
                   you CLIP from the screen with your mouse.





         Phoenix           Technical Reference Manual        Page 104

                   You can edit, view, save, reload, and feed the file  
                   names  back  to  the  BBS when  you  are  ready  to  
                   download.

                   The Download Clipboard has 64 FILE cells. Each file  
                   cell can hold ONE file name.

                   Almost all the Download Clipboard functions work on  
                   TAGGED  files. A tagged file is highlighted,  black  
                   with  an  off-white background. Other  file  names,  
                   those  not  tagged, are bright white with  an  off- 
                   white background.

                   To tag a file, move to its cell and click the  LEFT  
                   mouse button. To untag a file, move to its cell and  
                   click on it with the LEFT mouse button.

                   EXITING The Clipboard
                   ---------------------

                   There  are two way to exit the Download  Clipboard.  
                   Click  your RIGHT mouse button or click on  F2-Send  
                   Names with the LEFT mouse button.

                   FUNCTION KEY OPTIONS
                   --------------------

                   F2-Send Names

                   When the BBS asks you for the name or names of  the  
                   files  to  download, you can send  those  names  by  
                   opening the Download Clipboard and TAGGING the file  
                   names  you want to download. Once you  have  TAGGED  
                   all the files, click on the text "F2-Send Names" or  
                   press F2.

                   If  the  Phone  Book  Separation  Field  does   not  
                   indicate  what  to use, a small  window  will  open  
                   asking  if  you  want to use a  CR/LF  sequence  to  
                   separate the file names, click on YES if you do. If  
                   you  click on NO,  I will use a SPACE  to  separate  
                   the file names. Which to use can be confusing. Some  
                   BBS  packages  require the  CARRIAGE  RETURN,  some  
                   require  the  SPACE.  Experimenting  with  the  BBS  
                   you're  call  is  the  only  sure  fire  method  of  
                   determining which one is appropriate.

                   Once  you have selected the  separation  character,  
                   you  will return to TERMINAL mode and I  will  send  
                   the names of the files.




         Phoenix           Technical Reference Manual        Page 105

                   You may also move the mouse cursor to the text "F2- 
                   Send  Names"  and click the LEFT  mouse  button  to  
                   select this option.

                   F3-Load Clip

                   This  function  allows  you to  RELOAD  a  Download  
                   Clipboard  that you previously saved with  the  F6- 
                   Save option.

                   A  FILEBOX will open listing all the CLIPBOARDS  in  
                   the  current directory. 

                   F4-Clear

                   This clears the Download Clipboard. If you want  to  
                   SAVE  the names of the files you have clipped  from  
                   the screen, use the F6-Save option before  pressing  
                   F4.

                   You may also move the mouse cursor to the text "F4- 
                   Clear"  and click the LEFT mouse button  to  select  
                   this option. 

                   F5-Clear Tagged

                   This option is similar to F4 except it only removes  
                   the file names you have TAGGED. The remaining  file  
                   names are shifted up to fill the blank cells.

                   This is useful if you tag a bunch of files but  can  
                   only download a few at a time. After each download,  
                   select  F5-Clear Tagged to remove the names of  the  
                   files you just download and tag a new group.

                    You  may  also move the mouse cursor to  the  text  
                   "F5-Clear  Tagged" and click the LEFT mouse  button  
                   to select this option.

                   F6-Save

                   The Save option allows you to save the contents  of  
                   the  current Download Clipboard to disk, maybe  you  
                   did not have enough time to download the files  you  
                   wanted.

                   A  small window will open asking for a  file  name.  
                   You may enter up to 8 characters, but do NOT  enter  
                   an EXTENSION. I will add the file extension of CLP.  





         Phoenix           Technical Reference Manual        Page 106

                                    Upload Clipboard

                   The  Upload Clipboard, used when you upload with  a  
                   Batch Protocol, is divided into three groups,  each  
                   group comprising a PATH and 25 FILES cells.

                   The  3  different  PATH  fields  are  automatically  
                   initialized  to the values defined in TERM.CFG.  If  
                   you failed to define the paths, they will be blank.  
                   A Blank PATH field uses the current directory. 

                   The three groups work independently of each  other.   
                   By this, I mean that you could specify files in the  
                   1st and 3rd groups without having to specify  files  
                   in the 2nd group.  Maybe you only want to send from  
                   the 2nd group, and that is fine too.

                   The  PATH  cells are like the FILES cells  in  that  
                   they  can be changed.  You may decide to leave  one  
                   of  the  3 default paths blank, just  in  case  you  
                   frequently    upload   from    several    different  
                   directories depending on who you call.  This  would  
                   save time clearing a PATH field all the time.

                   Each  FILES cell can contain exactly  one  filename  
                   specification.   8 characters for the NAME, the  .,  
                   and  3 characters for the EXTENSION.  However,  you  
                   do not have to use all 12 characters.

                   You should NEVER use the wildcard characters *  and  
                   ?   in  a  CELL unless you plan  on  using  the  F2  
                   option. Not all protocol drivers support  expanding  
                   wildcard   characters.  I  believe  most   of   the  
                   protocols in this version do, but future  protocols  
                   (new ones) may not.

                   I will validate the file name. If the file does not  
                   exist,  you will hear a beep and I will  clear  the  
                   cell.

                   Care  should be taken when changing a PATH cell  if  
                   you have files defined in that GROUP.

                   FUNCTION KEY OPTIONS
                   --------------------

                   F2-File List  







         Phoenix           Technical Reference Manual        Page 107

                   When  the cursor is in a FILES cell, you can  press  
                   F2  to  obtain a list of available files.   If  the  
                   cell  is blank, a default of *.* is  used,  showing  
                   all the available files in that PATH group.  If the  
                   cell contains a filename with wildcard  characters,  
                   such as *.C, then all the files that end in .C  are  
                   shown in the Filebox.  

                   F3-Load Clip  
 
                   This  option  will  present  you  with  a  list  of  
                   previously  saved,  with F5, clipboards.  

                   F4-Clear  

                   This clears all FILE cells and PATH cells.

                   F5-Save To Disk

                   This  will  create  a file, you will  be  asked  to  
                   provide  the name, containing the contents  of  the  
                   current clipboard. You may reload the clipboard  at  
                   a later date using F3-Load Clip.

                   When you are asked to provide the file name, do NOT  
                   include any type of extension. I will use a default  
                   extension  of .ULP so that it can be identified  as  
                   an UPLOAD clipboard board when you select to  load,  
                   F3-Load Clip.

                   F10-Done

                   If  you  selected to EDIT the Clipboard,  ALT-E  or  
                   Mouse  Menu  Option, you will  return  to  terminal  
                   mode. 

                   MOUSE KEYS

                   Clicking  LEFT  mouse  button  simulates   pressing  
                   ENTER,  clicking  MIDDLE  mouse  button   simulates  
                   pressing ESC and clicking RIGHT mouse button active  
                   mouse cursor.

                   When the mouse cursor is active, you can select any  
                   of  the  F-KEY options by moving to  the  text  and  
                   clicking  the  left mouse button. To  deactive  the  
                   mouse  cursor  without  selecting  anything,  click  
                   right mouse button.






         Phoenix           Technical Reference Manual        Page 108

                   MOVING BETWEEN CELLS
                   --------------------

                   UP  ARROW, moves you to the CELL above the one  you  
                   are currently in. If you are in the TOP Cell on the  
                   screen, you will move to the BOTTOM most cell.

                   DOWN ARROW, moves you to the CELL below the one you  
                   are  currently  in. If you are in the  BOTTOM  most  
                   cell on the screen, you will move to the TOP cell.

                   CTRL LEFT ARROW, moves you one cell to the LEFT. If  
                   you  are  already at the left most cell,  you  will  
                   cycle to the right most cell on the same ROW.

                   CTRL RIGHT ARROW, moves you one cell to the  RIGHT.  
                   If you are already at the right most cell, you will  
                   cycle to the left most cell on the same ROW.

                   ENTER, moves you one cell to the RIGHT. If you  are  
                   already  at  the right most cell, you move  to  the  
                   left most cell on the next line. If you are already  
                   ON  the last line, you will cycle to the  TOP  most  
                   cell.

                   CTRL-HOME, moves you to the first cell.

                   CTRL-END, moves you to the last cell.

                   ALT1, Jumps directly to the PATH cell for the first  
                   GROUP.

                   ALT2,  Jumps  directly  to the PATH  cell  for  the  
                   second GROUP.

                   ALT3, Jumps directly to the PATH cell for the third  
                   GROUP.

                   CELL EDITING KEYS
                   --------------------

                   ESC, Clears the current cell.

                   Left Arrow, move one character to the left.

                   Right Arrow, move one character to the right.

                   HOME, move to first character in cell.

                   END, move to the last character in cell.

                   DEL


         Phoenix           Technical Reference Manual        Page 109

                   BackSpace

                   Enter, move to next cell. 

                                   Send Log-In String

                   This sends the LOG-ON Macro, the one you defined in  
                   the phone book record for this BBS.

                                     Screen Snapshot 

                   This takes a 25x80 snapshot of the current  screen.  
                   A  window will open and a default filename will  be  
                   displayed.  If  you want to use  that  name,  press  
                   RETURN or click LEFT mouse button.

                   If you want to use a different filename, press  ESC  
                   or  click MIDDLE mouse button and type in  the  new  
                   file name.

                   If  the file already exists, the snapshot  will  be  
                   appended to it.

                                     Paste From File

                   This  function will allow you to send the  contents  
                   of a text file as if you had typed it in.

                   A window will open asking for the name of the file,  
                   it  must be in the current directory. If you  can't  
                   remember  the  name, press ENTER  without  entering  
                   anything  and  I'll show you a list of  the  files,  
                   sorted by name, in the current directory.
                             
                   One  possible  use  for  this  function  would   be  
                   preparing for an upload prior to calling the BBS.

                   You  could  enter the descriptions, and  any  other  
                   information the BBS may ask you, offline. After, or  
                   before  depending  on  the BBS  software,  you  can  
                   simply paste the text file to fill in the questions  
                   the BBS asks. 

                   For  example, lets assume you are going  to  upload  
                   the file TEST.ARJ to an Osiris system.

                   Osiris requires the information prior to the upload  
                   to   prevent  you  from  wasting   time   uploading  
                   duplicate files and to guaranty a file  description  
                   in case you drop carrier.




         Phoenix           Technical Reference Manual        Page 110

                   You could prepare this off-line:

                   TEST.ARJ
                   NThis is a test upload
                             
                   When you select the Upload function and Osiris  ask  
                   for the name of the file, paste this text file  and  
                   it will provide all the information.

                   The  first  line  answers  the  "Enter  File  Name"  
                   question.

                                       Information

                   Opens   a  window  on  the  screen   showing   Uart  
                   information, Log status, connect rate, and  several  
                   other pieces of information.

                               Shift F1 Throught Shift F10

                   The  Shift F1 thought Shift F10 keys are linked  to  
                   external batch files of the same name. 

                   E.g., SF1.BAT, SF2.BAT, . . . SF10.BAT.

                   This  gives  you the ability to  hook  an  external  
                   application  into  the terminal program such  as  a  
                   text editor, spreadsheet, wordprocessor, etc.

                   Shift  F1 through Shift F10 does not pass  augments  
                   to  the external batch files. If you need  to  pass  
                   arguments, see the next section.

                                 Alt F1 Throught Alt F10

                   ALT F1 thought ALT F10 keys are linked to  external  
                   batch files of the same name. 

                   E.g., AF1.BAT, AF2.BAT, . . . AF10.BAT.
                             
                   This  gives  you the ability to  hook  an  external  
                   application into the terminal program.

                   The primary difference between SHIFT F keys and ALT  
                   F keys is the ability to pass arguments. 

                   I  will pass the following arguments to  the  batch  
                   files:

                   %1 - Serial Port Number.
                   %2 - Serial Port Speed.
                   %3 - Connect Rate.


         Phoenix           Technical Reference Manual        Page 111
                              
                   You  also  have  the option  of  adding  additional  
                   arguments prior to calling the batch file.

                   A  window will open and I'll ask you if  you  would  
                   like  to provide any additional arguments.  If  you  
                   do,  type in the what you want passed to the  batch  
                   file.

                   Additional arguments will be passed in %4, %5,  %6,  
                   %7, %8, and %9.

                   If  you haven't guessed, %1, %2, . . . %9  are  DOS  
                   BATCH parameters.

                   The goal is to allow external applications HOOKS to  
                   the  terminal  mode  and to  guaranty  that  serial  
                   information   can  be  made  available   to   those  
                   applications.

                   One  might surmise that this is how you would  hook  
                   in  extra  protocol drivers. Yes, that  would  work  
                   just fine but it wasn't the original concept.

                                    Mouse Screen Cut

                   This  allows  you  to CUT a small  section  of  the  
                   current  screen  to a text file (could be  used  to  
                   steal  taglines  if you have to read  messages  on- 
                   line, i.e., no TNT or QWK doors).

                   Move   the   mouse cursor to where  you  want   the   
                   CLIP  to start  and press the LEFT mouse button  to  
                   drop  the   CLIP anchor. Move the mouse  cursor  to  
                   where  you want the CLIP to  end, you may not  move  
                   to  the LEFT of your anchor  or above  the  anchor,  
                   and press the RIGHT mouse button.

                   As  you  move  your cursor, once  the  anchor   has   
                   been dropped,  the area that WOULD be considered as   
                   part  of the CLIP rectangle will be highlighted.
 
                   After  you  have pressed the  RIGHT  mouse  button,  
                   you'll  be asked for the name of the file to  write  
                   the   CLIP  to. The  default is TNT.cut and can  be  
                   selected  by  pressing RETURN or clicking the  LEFT  
                   mouse button.

                                 Phone Book

              Edit,  Kill, View, and CALL use a single routine to  get  
              the information on which phone book records you want  to  
              use.


         Phoenix           Technical Reference Manual        Page 112

              Nine  entries will be displayed at one. The  number  (1- 
              72),  the name of the BBS or service, the last time  you  
              called, the total time on-line with that BBS or service,  
              and finally whether or not that entry is tagged.

              There are six control buttons at the bottom of the page:  
              ASRT, ESC, PGDN, PGUP, HOME, END, and DSRT.

              ASRT means sort the book in ascending order, DSRT  means  
              sort the book in descending order.

              Press ESC or click on the ESC botton when done.

              You  can click on each botton to select it or press  the  
              hotkeys  A,  ESC, PGDN, PGUP, HOME, END or D.  With  the  
              exceptions  of A, ESC, and D, the remaining hotkeys  are  
              located on the keypad.

                                        Bbs Name

                   The name of the BBS or Service this record is for.

                                    Bbs Phone Number

                   The  number to the BBS or Service. If you  have  to  
                   dial  long  distance, be sure to include  the  long  
                   distance number, general 1, and the area code.

                                     Predial String

                   The Predial String lets you enter special  commands  
                   to  customize your modem (or dial a  long  distance  
                   access number). The Predial string is sent prior to  
                   the  dial command, the dial command being  ATDT  or  
                   ATDP.

                                    Default Protocol

                   To speed up selecting a protocol, when you elect to  
                   upload  or download, you can define which  protocol  
                   you want the cursor placed on.

                   To  accept  the default, press ENTER or  click  the  
                   left mouse button.

                   If  you need to use a different protocol, move  the  
                   scrollbar  (up arrow, down arrow, or mouse  cursor)  
                   to  the  protocol you would rather  use  and  press  
                   ENTER or click LEFT mouse button.

                   Pressing ESC or clicking middle mouse button aborts  
                   the selection.


         Phoenix           Technical Reference Manual        Page 113

                                      Log-On Macro
                             
                   LOG-ON Macro Field is a special field that you  can  
                   use to hold your name and password for the  system.  
                   When you get the first name prompt, just press ALT- 
                   N to send it. 
                        
                   The  Log-ON macro reserves two special  characters,  
                   preceded by ^.

                   ^M Send a carriage return.

                   ^~  Pause 1 second.

                   You  should NOT end your macro definition with  ^M.  
                   TNT  will automatically insert a CR at the  end  of  
                   the string.

                   E.g., JOHN DOE^M~Y^M~MYPASSWORD

                   This  will send JOHN DOE, a CARRIAGE  RETURN,  wait  
                   1/10th  of  a  second then SEND  Y  followed  by  a  
                   CARRIAGE  RETURN, wait 1/10th of a second and  send  
                   MYPASSWORD followed by a CARRIAGE RETURN.

                   This could be a log-on macro for an Osiris system.

                   A BETTER log-on macro for an Osiris system would be

                   JOHN DOE MYPASSWORD

                   A log-on macro for Remote Access would be

                   JOHN DOE^M~MYPASSWORD

                   Since most of you use script languages to log-on to  
                   the  BBS, this will take care of 99.99  percent  of  
                   your  needs  without having  to  learn  complicated  
                   scripts.

                                      Connect Time

                   Phoenix  tracks the number of minutes connected  to  
                   each  system. This field holds that time and is  in  
                   minutes.

                                      Times Called

                   Records the number of calls placed to the system.





         Phoenix           Technical Reference Manual        Page 114

                                       Last Called

                   Contains  the last date and time you were  on-line.  
                   You may not edit this field.

                                      Uart Settings

                   This  section  allows  you to  define  the  Parity,  
                   Wordlen,  and  stop bits to use when  calling  this  
                   person.

                   There  are 11 different settings, move to  the  one  
                   you  want  and  press return or  click  left  mouse  
                   button.

                   If you are calling a BBS, you generally ALWAYS  use  
                   None,  Eight, and One for the parity, wordlen,  and  
                   stop bits.

                   I will display, these settings as PWS or N81  which  
                   means:

                   Parity   = None
                   Wordlen  = Eight
                   Stopbits = One
                   
                                         Duplex

                   Most  systems you call will use FULL  Duplex.  This  
                   means  that everything you type is ECHOED  back  to  
                   you.  If you you are on a system and what you  type  
                   does  not appear on the screen, that  system  needs  
                   HALF Duplex.

                   Some  BBS  programs do not echo  MENU  options,  so  
                   don't let that throw you.

                                         Logfile

                   You  have the option of defining a  DIFFERENT  data  
                   capture log, session log in some circles, for  each  
                   system  you call. The Logfile can be any legal  DOS  
                   file name you want to use.

                   If you do not define a LogFile, the default will be  
                   TERM.LOG.

                                         Autolog

                   This tells me that you want the CAPTURE or  SESSION  
                   log turned on as SOON as you connect.



         Phoenix           Technical Reference Manual        Page 115

                   To  engage AutoLog, enter Y or y. N or n  means  do  
                   not engage AutoLog.

                   In  order  to  use AutoLog, Y, you  must  define  a  
                   LogFile. If NO LogFile is defined, AutoLog = Y will  
                   be ignored.

                                 File Separation Method

                   This is used by the download clipboard to determine  
                   whether  to separate the file names with a CR or  a  
                   SPACE.  Since this is a static option, there  is  a  
                   phone  book field for it. Enter C for CR and S  for  
                   space. 

                        Downloading And Auto-Virus Scanning

              When  you  exit  the  terminal  module,  your   download  
              directory will be rescanned.

              If  any new files show up, you'll be asked if  you  want  
              that file checked for virus infestation. 

              Assuming that you answer Y

              If the file is an archive; SQZ, ZIP, LZH, or ARJ it will  
              first be pulled apart to expose the files inside. If the  
              archive  could  NOT  be pulled  apart,  you'll  get  the  
              prompt:

              Bad Archive, Delete File <Y/n> ?

              SQZ.EXE, PKUNZIP.EXE, LHARC.EXE, and ARJ.EXE must be  in  
              the current directory or in a PATH directory. If one  of  
              the  programs  is not available, that  archive  will  be  
              treated as a normal file.

              Assuming,  sure doing a lot of assuming aren't  we,  the  
              archive  was  OK, the files inside the archive  will  be  
              checked for any known viruses. 

              If a virus is found you'll get the prompt:

              Virus detected, Delete File <Y/n> ? 

              The external program SCAN.EXE, included in this package,  
              is  used to check the files. This allows you  to  update  
              the virus scanner when a new one is released. Saves from  
              downloading a WHOLE new archive.

              Files that are not archives will simply be scanned.



         Phoenix           Technical Reference Manual        Page 116

              When  you  are asked about checking a file,  you  should  
              answer Y under the following conditions:

              1.  It is an archive having the file extension of  .ZIP,  
              
              2. It is an EXE, COM, OVL, or OVR.

              You  do not need to check .TXT, .DOC, .BAT, etc.  files.  
              Only EXE, COM, OVL, OVR files can contain viruses.  ALso  
              system drivers but they have no set file extensions.

              There is a nasty rumor going around that it is  possible  
              to place an infected file inside an archive and when you  
              extract  the  archive, a hidden file  will  execute  the  
              infected file.

              This is not true. At least it is not true with ARJ, ZIP,  
              and LZH files.  It is simply a rumor to spread fear  and  
              get people to stop checking for viruses.

              What  is  true  is  that you CAN do  this  with  a  self  
              extracting  archive by modifying the extractor to  auto- 
              execute  one  of the files inside  the  self  extracting  
              archive.

              Therefore,   you  should  avoid  downloading  any   self  
              extracting  archive. A self-extracting archive  has  the  
              file extension of EXE or COM. If it doesn't have one  of  
              those file extensions, it isn't dangerous.

                                 Terminal Emulation

              Phoenix  supports ANSI and TTY with limited  AUTO-DETECT  
              support for VT 52 and VT 100. 

              We  can justify this because 99.99 percent of  you  will  
              either call a BBS or on a commercial service. Since  all  
              BBS'  use ANSI or TTY and most commercial  services  use  
              TTY, there is no GREAT need to support everything  under  
              the sun.

                                      Keyboard

              The  keys  on  your KEYPAD, and  some  F-Keys,  will  be  
              remapped to VT52/VT100, they are both the same.

              If there is not a VT52/VT100 key for the KEYPAD key, the  
              key  will remap to WORDSTAR movement commands. Most  BBS  
              full   screen  editors  support  either  VT52/VT100   or  
              Wordstar commands. Some, such as Osage, support both.



         Phoenix           Technical Reference Manual        Page 117

              Below  is a list of keys, the mode they operate in,  and  
              what they do.

              Left  Arrow        VT100/VT52    Move one character  to  
                                               the left.

              Right  Arrow       VT100/VT52    Move one character  to  
                                               the right.

              Up Arrow           VT100/VT52    Move UP a line.

              Down Arrow         VT100/VT52    Move DOWN a line.

              HOME               Wordstar      Goto start of line.

              End                Wordstar      Goto end of line.

              Ctrl-HOME          Wordstar      Goto to TOP.

              Ctrl-END           Wordstar      Goto BOTTOM.

              PGUP               Wordstar      Goto Prior Page.

              PGDN               Wordstar      Goto Next Page.

              DEL                Wordstar      Delete character under
                                               cursor, pull rest of
                                               line back.

              INS                Wordstar      Insert a blank under
                                               cursor, shift rest of
                                               line forward.
              F1                 VT100/VT52    Emulates PF1.

              F2                 VT100/VT52    Emulates PF2.

              F3                 VT100/VT52    Emulates PF3.

              F4                 VT100/VT52    Emulates PF4.

                                  Script Language

              There  is  none.  Having  developed  and  sold  terminal  
              programs, either under our own brand name or licensed to  
              others for resale, we have found that 99 percent of  the  
              people used the script language to enter their names and  
              passwords on the BBS.

              Since the majority used it for that purpose, we included  
              a  LOG-IN Macro, phone book record for each  system  you  
              call, that is easy to set-up and even easier to use, the  
              biggest complaint about the script languages was "It  is  
              to complicated". Well, it isn't anymore.

         Phoenix           Technical Reference Manual        Page 118

              Anyway,  we  have decided not to waste  time  developing  
              something  for  TNT that so few will  use.  We'd  rather  
              spend that time adding in features that the majority  of  
              you will find useful.

                                      Call.log

              When  you  CONNECT to a BBS or Service  the  day,  date,  
              time, who you connected to, when you disconnect, and how  
              long (in minutes) you where on-line will be added to the  
              CALL.LOG.

              Example

              Wednesday May 20, 1992 Called Vetlink Iii at 03:10 AM.
              Disconnected at 03:10 AM, on-line 1 minutes.

              Wednesday May 20, 1992 Called Vetlink Iii at 03:15 AM.
              Disconnected at 03:17 AM, on-line 3 minutes.

              Wednesday May 20, 1992 Called Vetlink Iii at 03:26 AM.
              Disconnected at 03:30 AM, on-line 4 minutes.

              Wednesday May 20, 1992 Called Vetlink Iii at 12:58 PM.
              Disconnected at 01:00 PM, on-line 2 minutes.

                                      Filebox

              A  number of subsystem's use a FILEBOX. This  lists  the  
              names of the files in a specific directory that you  can  
              TAG.

              Using  this is fairly simply, just point and  shoot.  If  
              you want to HOTKEY it, use the arrow keys to move, press  
              ENTER for OK, and C for Cancel.

                                      Dialing

              When  you  are  actually dialing,  you  can  HOTKEY  the  
              bottoms DIAL NEXT, ABORT, and REMOVE by using the  first  
              letter: D, A, and R.

         

                              Advanced Operations

         Phoenix  has several features specifically for  the  advanced  
         system  operator. Unless you KNOW what you are doing,  we  do  
         not recommend that you mess with these features.

                                       Nomail



         Phoenix           Technical Reference Manual        Page 119

              If  the file "NOMAIL" exists in the  Phoenix  directory,  
              Phoenix will not attempt to place any outbound call  nor  
              will it accept an INBOUND call.

              Only ONE line may actual PROCESS inbound mail and  build  
              outbound messages for ALL the other lines. 

              By  creating  a NOMAIL file, the contents  of  the  file  
              isn't  important, the line that IS processing  the  mail  
              can  prevent the OTHER lines from interfering with  that  
              processing  by  accepting  inbound calls  or  trying  to  
              deliver echomail bundles that you MAY be in the  process  
              of  updating. See the section on NETCOM.EXE for  further  
              details.
                                     Recycle.xxx

              Recycle.xxx,  xxx  would be replaced with  the  3  digit  
              (padded   with  ZEROS)  BBS  Node  number   defined   in  
              CONFIG.EXE, is used by an external application to  FORCE  
              phoenix  to  rescan  the matrix  area  and  reroute  the  
              messages.

              Assuming that you have two mailers, one running on  NODE  
              1  and one  running on NODE 2. NODE 1 does ALL the  mail  
              processing (unpacking PKTS, processing inbound Echomail,  
              TICS, etc.) and it just imported and exported  echomail.  
              You  would  want  NODE 2 to rescan the  matrix  area  to  
              PICKUP  those new echomail bundles and you want it  done  
              now.

              Using NETCOM, see section on netcom.exe for details, you  
              would create the file RECYCLE.002

              When  NODE 2 SEES that file, it will rescan  the  matrix  
              area and find the new messages.

              Phoenix  ONLY scans for the RECYCLE.xxx file once  every  
              60  seconds  so  there  may be  a  slight  delay  before  
              anything happens. 















         Phoenix           Technical Reference Manual        Page 120

                                    Sysdown.xxx

              Sysdown.xxx,  xxx  would be replaced with  the  3  digit  
              (padded   with  ZEROS)  BBS  Node  number   defined   in  
              CONFIG.EXE, is used by an external application to  FORCE  
              Phoenix  to  EXIT with errorlevel 6.

              Sysdown  could  be used when you have   BBS  maintenance  
              events on multiple line systems. You want ALL lines down  
              during  message area PACKING (removing delete  message),  
              USER record maintenance (deleting old user records), and  
              other  operations that would simply not work if you  had  
              callers on-line.

              Phoenix  ONLY scans for the SYSDOWN.xxx file once  every  
              60  seconds  so  there  may be  a  slight  delay  before  
              anything happens. 

              See the section on NETCOM.EXE for further details.



































         Phoenix           Technical Reference Manual        Page 121

                           Special Phoenix Flag Settings

              You'll  find  an option, config.exe, on  the  main  menu  
              , second page.  This takes to you another  CONFIGURATION  
              screen with the following settings:

              ECHOMAIL.BAT YES/NO
              TIC.BAT YES/NO
              AFIX.BAT YES/NO
              RAID YES/NO
              UNBUNDLE MAIL YES/NO

              If  you are running more than one mailer, you  can  only  
              have  ONE of them actual do the inbound  processing  for  
              Echomail,  TIC,  RAID, AREAFIX,  and  Unbundling  matrix  
              mail.

              By  TOGGLING these options to NO, you can  select  WHICH  
              mailer will do the actual inbound processing.

                                   Crash = Direct

              If  you are using Phoenix with applications that do  not  
              support  the  DIRECT matrix message flag, you  can  have  
              and message flagged as CRASH to automatically be flagged  
              as DIRECT.


                                     Netcom.exe

              NETCOM  is  an application you can use to  run  multiple  
              copies of Phoenix and allow all LINES to handle  inbound  
              and outbound mail.

              NETCOM requires two command line arguments, one if  MOVE  
              is used.

              The  first  argument  is  the  COMMAND;  WAIT,  SHUTDOWN,  
              RECYCLE, FREE, NOMAIL, COPY, or MOVE.

              The second argument, with the exception of MOVE, is  the  
              NODE number you defined for the Mailer who's batch  file  
              you are currently in.

              That is a little bit confusing but it will become  clear  
              later on.

              The only command that doesn't require the node number is  
              MOVE.





         Phoenix           Technical Reference Manual        Page 122

                                      Wait <Node #>

                   Wait  until the NODE that called for  the  SHUTDOWN  
                   says it's ok to go back on-line.

                                    Shutdown <Node #>

                   Tells  the  OTHER  mailers that <NODE  #>  said  to  
                   SHUTDOWN and exit with ERRORLEVEL 6.

                                    Recycle <Node #>

                   Tells  the  OTHER  mailers that <NODE  #>  said  to  
                   RESCAN their matrix areas.

                                      Free <Node #>

                   Tells  the OTHER mailers that <NODE #> said it  was  
                   OK  to go back ON-LINE or that it is OK  to  accept  
                   and place mail calls.

                   This  should ONLY be used by the NODE  that  CALLED  
                   for the SHUTDOWN or the freeze on MAIL sessions.

                                     Nomail <Node #>

                   Tells  the OTHER mailers that <NODE #> said NOT  to  
                   accept or place mail calls.

                                      Copy <Node #>

                   Move  all the files in the OTHER  mailer's  inbound  
                   directory to <NODE #>'s inbound directory.

                                          Move

                   Move  MATRIX messages to specific  individual  from  
                   the PRIMARY matrix area to the matrix area for  the  
                   mailers those individual are assigned to.

              NETCOM.EXE  requires a control file, NETCOM.CFG, and  if  
              MOVE is used,  NETCOM2.CFG.

                                       Netcom.cfg

                   NETCOM.CFG contains information (node number,  path  
                   to  system  files, and path to  the  inbound  area)  
                   about each mailer you have on-line.






         Phoenix           Technical Reference Manual        Page 123

                   The format:

                   <NODE #> <SYSTEM PATH> <INBOUND PATH>

                   You can define UPTO 8 Nodes, 1-8.

                   Example:

                   1 c:\mailer1 c:\mailer1\in
                   2 c:\mailer2 c:\mailer2\in

                                       Netcom2.cfg

                   This  file contains the path to the PRIMARY  matrix  
                   area  (this is the matrix area for the mailer  that  
                   does the inbound processing), the DOMAIN address of  
                   individual systems, and the path to the MATRIX area  
                   they are assigned to.

                   If NETCOM finds a message addressed to one of those  
                   addresses, it moves it to the correct matrix  area.  
                   If  the  address isn't listed  in  NETCOM2.CFG,  we  
                   assume it is already IN the correct matrix area.

                   Example:

                   c:\mailer1\matrix
                   1.237.504.0 c:\mailer3\matrix
                   1.100.10.0 c:\mailer2\matrix
  
                   You can list a MAXIMUM of 50 systems.

              When  NETCOM  issues a NOMAIL or  SHUTDOWN  command,  it  
              requires all nodes to RSVP the command.

              NETCOM  will LOOP until all nodes reply with  their  own  
              RSVP'S.  That allows nodes that are already  BUSY  doing  
              something to finish whatever it is they are doing.

              Here  are  a couple of examples that you can  use  as  a  
              guideline for this program.

              You are running TWO mailers and the first mailer is NODE  
              1 and the second mailer is NODE 2.

              The first mailer is in the directory c:\mail1 and the  
              second  mailer is located in the directory c:\mail2.  If  
              you  run multiple mailers, they have to be in  different  
              directories.

              The  first mailer uses C:\MAIL1\INBOUND for its  inbound  
              directory and the second mailer uses C:\MAIL2\INBOUND as  
              its inbound directory.

         Phoenix           Technical Reference Manual        Page 124

              If you run multiple mailers and you are allowing SERVICE  
              requests  or  file request, you HAVE  to  use  different  
              inbound  directories.  If  you  do  NOT  allow   service  
              requests  or  file requests, they can all use  the  same  
              inbound directory.

              The  first  mailer uses c:\mail1\matrix for  its  matrix  
              directory and the second mailer uses c:\mail2\matrix for  
              its matrix area. You HAVE to use different matrix  areas  
              for each mailer.

              To run multiple mailers, you have to decide which of the  
              mailers  is going to do the inbound processing.  Inbound  
              processing  means  unbundling  matrix  mail,   echomail,  
              processing TIC/RAID/AREAFIX requests.

              Only  ONE mailer can do that, the rest must  ignore  the  
              presents of PKT's, ECHO ARCHIVES, TICS, etc.

              Lets  say the first mailer is going to be the  one  that  
              does the inbound processing.

              Log into the directory that contains the 2nd mailer  and  
              run CONFIG.EXE. Select the MORE box and when the  second  
              screen  comes up, set ECHOMAIL.BAT,  TIC.BAT,  AFIX.BAT,  
              RAID,  and UNBUNDLE MAIL to NO. This will cause the  2nd  
              mailer  to  ignore the presents of TIC,  RAID  REQUESTS,  
              AREAFIX REQUESTS, ECHOMAIL, and PKTS.

              Next  you have to decide WHO'S mail is going to be  held  
              for  pickup by which mailer. While it WOULD be  nice  to  
              allow  them  to  use EITHER, that  just  isn't  possible  
              without a lot of extra code. Since this is not going  to  
              be  something  a lot of people do, we don't want  to  do  
              that.

              Lets  say  1.100.10.0 will get his mail from  the  first  
              mailer  and 1.200.5.0 will get his mail from the  second  
              mailer.

              Create  a  text file called NETCOM2.CFG  and  enter  the  
              following:

              C:\MAIL1\MATRIX
              1.200.5.0 C:\MAIL2\MATRIX
              <EOF>

              The  first line points to the matrix area  belonging  to  
              the mailer that will be processing inbound mail. In this  
              case, that would be the 1st mailer.




         Phoenix           Technical Reference Manual        Page 125

              The second line  contains the domain address followed by  
              the path to the Mailer's matrix area HE will be calling.  
              In this case, the 2nd mailer.

              <EOF> means end of file and you don't enter that.

              If  you had more than one, you would list  each  person,  
              one to a line, a maximum of 50 lines.

              E.g.

              C:\MAIL1\MATRIX
              1.200.5.1 C:\MAIL2\MATRIX
              1.200.5.2 C:\MAIL2\MATRIX
              1.200.5.3 C:\MAIL2\MATRIX
              <EOF>

              If you had THREE mailers

              C:\MAIL1\MATRIX
              1.200.5.1 C:\MAIL2\MATRIX
              1.200.5.2 C:\MAIL3\MATRIX
              1.200.5.3 C:\MAIL2\MATRIX
              <EOF>
              
              Notice  that NONE of the paths end with a \ ?  You  must  
              use a LEGAL DOS PATH.

              The next step would be to create file called NETCOM.CFG.

              This file contains; The Mailers Node number, the path to  
              the  mailer's directory, and the path to  that  mailer's  
              inbound area.

              E.g.
              
              1 C:\MAIL1 C:\MAIL1\INBOUND
              2 C:\MAIL2 C:\MAIL2\INBOUND

              Notice  that NONE of the paths end with a \ ?  You  must  
              use a LEGAL DOS PATH.

              Ok, lets put all this to get so that the 1st mailer  can  
              process echomail for both lines.

              Eg. the ECHOMAIL.BAT file for the first mailer.








         Phoenix           Technical Reference Manual        Page 126


              NETCOM NOMAIL 1
              NETCOM COPY 1
              *
              *
              * Process Echomail and whatever else.
              *
              *
              NETCOM MOVE
              NETCOM RECYCLE 1
              NETCOM FREE 1
              <EOF ECHOMAIL.BAT>

              The  first line, "NETCOM NOMAIL 1" tells all  the  other  
              mailers that NODE 1 says NOT to process any mail, in  or  
              out.

              The second line, "NETCOM COPY 1" copies all the files in  
              the  inbound directories for the OTHER mailers, in  this  
              case  the 2nd mailer, to the inbound directory for  NODE  
              1. 

              This copy does NOT overwrite existing files. If the file  
              already  exists in NODE 1's inbound directory, the  copy  
              will be skipped.

              This  allows NODE 1 to process anything that came in  on  
              the other nodes.

              The lines beginning with '*' would be where you'd  place  
              your normal echomail processing instructions.
              
              The  8th line, "NETCOM MOVE" scans the matrix area,  the  
              one  that was defined (first line) in  NETCOM2.CFG,  and  
              moves  any  message addressed to anyone  listed  in  the  
              NETCOM2.CFG file to the matrix area on the node they are  
              assigned to.

              The  9th  line, "NETCOM RECYCLE 1" tells all  the  other  
              mailers  that NODE 1 wants them to RESCAN  their  matrix  
              areas  to pickup any messages that "NETCOM  MOVE"  might  
              have placed there.

              The  10th and final line, "NETCOM FREE 1" tells all  the  
              other mailers that NODE 1 said it was OK to process mail  
              again.

              You would do the exact same thing for TIC, AREAFIX,  and  
              RAID requests.

              What about Midnight maintenance type events? With  those  
              types of events, you can't have the other lines running.


         Phoenix           Technical Reference Manual        Page 127
              
              Well  that is where the SHUTDOWN and WAIT commands  come  
              into play.

              Again,  only one mailer should know anything  about  the  
              maintenance event.

              Lets say the 1st mailer, mailer was defined (config.exe)  
              as NODE 1, will also handle external maintenance  events  
              and your event is set to exit errorlevel 50.

              Phoenix
              If errorlevel 50 goto maint
              *
              :MAINT
              NETCOM SHUTDOWN 1
              *
              NETCOM FREE 1

              The First line, "NETCOM SHUTDOWN 1" tells all the  other  
              nodes  that NODE 1 said to SHUT DOWN ASAP.  When  NETCOM  
              issues a SHUTDOWN command, it will pause for 65  seconds  
              to give the other nodes time to comply.

              The last line, "NETCOM FREE 1" tells the other nodes  it  
              is OK to go back on-line.

              The  BATCH  files  for  the  OTHER  mailers  would  look  
              something like THIS:

              :TOP
              PHOENIX
              IF ERRORLEVEL 6 goto WAIT
              *
              *
              :WAIT
              NETCOM WAIT 2
              GOTO TOP

              When a NETCOM SHUTDOWN is received, Phoenix always exits  
              with errorlevel 6. Trap that and jump to the label WAIT

              The line "NETCOM WAIT 2" instructs NETCOM to cycle until  
              until  the NODE that called for the SHUTDOWN says it  is  
              OK  to  go back on-line. The 2 is the  NODE  number  you  
              defined in CONFIG.EXE for THAT mailer.

                                   Screen Blanker

              Phoenix  has an internal screen blanker that will  blank  
              the  screen  when 5 minutes has elapsed  without  serial  
              port or keyboard activity.



         Phoenix           Technical Reference Manual        Page 128

              Pressing  a  key,  any serial activity,  or  placing  an  
              OUTBOUND call with automatically reactivate the screen.

              To FORCE the screen to BLANK, press B.


                                     Robot

         ROBOT.EXE  is a small program that automates the  sending  of  
         files  with  the same name that change on a weekly  or  daily  
         bases,   NODEDIFS,  NEWSLETTERS,  REPORTS,  DATABASE   FILES,  
         SPREADSHEETS, etc.

         ROBOT  handles this by tracking the date and time  stamps  of  
         each file it sends in a small database (ROBOT.DAT).

         Prior  to  SENDING the file, it checks  the  files  date/time  
         stamp  against  the  one  in  the data  base  and  if  it  is  
         different, the file is sent.

         ROBOT will flag the messages as NORMAL, DIRECT, FILE  ATTACH.  
         You can, using an optional command line switch, have the file  
         attaches flagged as CRASH.
 
         Robot needs to know WHO to send the file(s) to and you supply  
         that information in a control file, the name is up to you.

         Each  line  in  the control file  contains  a  single  DOMAIN  
         address.

         E.g.

         1.200.10.0
         1.300.10.0
         1.400.33.2

         To SEND a file, use the command line 

         ROBOT /S <File name> <Ctrl File Name>

         <FILE  NAME> is the name of the file to send. You can  use  a  
         full path, e.g. C:\PHOENIX\WORKSHEET.SPL

         You can also include DOS wildcard characters, e.g.

         C:\PHOENIX\WORKSHEET.*

         ROBOT also supports three additional command line arguments, /I  
         , /C, and /R <File Name>





         Phoenix           Technical Reference Manual        Page 129

         /I Clears the DATE/TIME stamps for every file in the database. 

         /R  <File Name> clears the DATE/TIME stamp for  <File  Name>.  
         This  lets  you resend the same file even  if  the  date/time  
         stamp on that file has not changed.

         /C Mark the message as CRASH.

                           Getting A Test Drive Key

         Phoenix  has  THREE modes; Registered, Test  Drive,  and  BBS  
         Front End.

                                  Test Drive Mode

              In  this mode, Phoenix is FULL function for a period  of  
              31  days.  At  the END of the 31 day  period,  you  must  
              either purchase the product or stop using it.

              While it would be NICE to just take everyone's word that  
              they  WILL comply with the above, life just  isn't  that  
              simple.

              To  GET  Phoenix  to run in TEST Drive  mode,  you  must  
              obtain a special TEST drive key.

              To get a TEST drive key, log onto one of the BBS' listed  
              in  the KEYSITE.DOC doc file. You'll find an  option  on  
              the  BBS' main menu for generating a Phoenix TEST  drive  
              key.

                                 Bbs Front End Mode

              If  you  do NOT have a REGISTERED Phoenix or  Your  TEST  
              Drive key has expired, Phoenix will operate in FRONT END  
              mode.

              In  FRONT END mode, Phoenix will not accept  an  inbound  
              mail session. However, it WILL pass HUMANS to your BBS.

              If  you  do not intend to use Phoenix as a  mailer,  but  
              simply to PASS HUMANS to your BBS, you are not obligated  
              to  purchase the program and may use it as long  as  you  
              like.
                                     Price

         The  price for Phoenix v3.0 is 89.95. This includes  all  bug  
         fixes and maintenance release. A bug fix can be identified by  
         the last digit in the version number. 





         Phoenix           Technical Reference Manual        Page 130

         A maintenance release can be identified by the second to  the  
         last digit in the version number.

         Major          Bug Fix Digit.
            Revision    v
            Digit -> X.YY
                       ^
                       Maintenance Digit.

         Upgrading  to  new MAJOR revisions, $45.00.  Major  revisions  
         come out every 12 to 16 months.

                               Technical Support

         If you have problems, you can leave a message to the sysop on  
         on one of the BBS' listed KEYSITE.DOC.

         You  may also call the voice number, 1-314-686-0154,  between  
         1  PM  and  8 PM CDT (Mon-Thu). To give  you  the  BEST  help  
         possible,  our programmers pull double duty and  also  answer  
         technical  questions. However, there may be times  when  they  
         are  not available to answer the phone. If that is the  case,  
         try calling later or use the BBS.

                                File Structures
                               Matrix Message Header

              We've already listed the file structure for the  message  
              headers. The following information should help you  work  
              with and create compatible matrix messages.

              Applications  MUST  make use of both the .attr  and  the  
              TYPE bit flag settings.
              
              In  other words, you MUST identify the TYPE of  message.  
              Phoenix  uses  the  TYPE field  in  the  Packet  control  
              system, the ROUTE manager, and the PACKER.

              The .attr flag 0x2000 gives you a way of telling Phoenix  
              NOT  to send the actual message. It is  understood  that  
              you would only use this flag setting with FILE ATTACHES.
             
              That  reduces  the  number of do  nothing  messages  the  
              receiver has to content with.

              You  do NOT have to use the 0x2000 .attr flag  with  the  
              following .type flags.

              0x0002 FILE REQUEST
              0x0004 ECHOMAIL BUNDLE
              0x0008 SERVICE REQUEST



         Phoenix           Technical Reference Manual        Page 131

              Phoenix  will not send the message used to attach  these  
              TYPES of messages. If it has to, it will create and send  
              a NULL bundle.

              Programmers  should  KEEP IN MIND that the  .attr  crash  
              flag  does  NOT bypass routing. If you do not  want  the  
              message routed, you MUST use the .attr DIRECT flag.

              Phoenix  automatically  deletes the *.MSG after  it  has  
              been  sent.  You do not have to CHECK any type  of  SENT  
              flags, they aren't needed.

              To  maintain  compatible with Fidonet and to  allow  for  
              full  zone, net, node, and point support; you must  ALWAYS  
              include the INTL, FMPT, and TOPT matrix kludges.

              The INTL Kludge is ALWAYS used, even if the  Destination  
              zone is the same as the Origin zone. Generally you  only  
              use  it  when  the zones are different.  But,  to  FULLY  
              support concurrent domains, the INTL kludge must  always  
              be used.

              FMPT Kludge is used when the Origin POINT is NONE ZERO.

              TOPT  Kludge is used when the Destination point is  NONE  
              ZERO.

              Format for each Kludge:

              D=Destination, O=Origin, H=HEX

01HINTL<SPACE><DZone>:<DNet>/<DNode><SPACE><OZone>:<ONet/Onode>0DH


              01HFMPT<SPACE><OPOINT>0DH
              01HTOPT<SPACE><DPOINT>0DH

              Be sure that EACH kludge line begins with 01H  and  ends  
              with  0DH. ALso make sure that you only use  ONE  kludge  
              per line and that is the ONLY thing on the line.


              Position  in the message generally isn't  important,  at  
              least it isn't for any of our mailers. But just to  play  
              it safe, you might want to place them BEFORE any text.









         Phoenix           Technical Reference Manual        Page 132

                                    Phoenix.cmd
struct _config
{
char mailer[30];
char sysop[20];
unsigned ZONE;
unsigned NET;
unsigned NODE;
unsigned POINT;
int port;
long baud;
long lock_rate;
char matrix_path[51];
char inbound_path[51];
char shell_line[51];
char use_rts_flow;
int min_baud;
long delay_in;
long delay_out;
long dial_delay;
char m_in[41];
char m_out[41];
char m_dial[41];
char m_answer[41];
char offhook;
int  max_calls;
int  uart_size;
char connect_strings[51][31];
long serial_rate[51];
int  max_busy;
long inbound_time_out;
char internet[81];
char files[13];
char echomail;
char fidonet;
char routing_type; 
unsigned aka_ZONE[4];
unsigned aka_net[4];
unsigned aka_NODE[4];
unsigned aka_POINT[4];
char secure_addressing;
unsigned char bbsnode;
unsigned flag1;
unsigned flag2;
int unused1;
int unused2;
long unused3;
long unused4;
char unused5;
char unused6;
};



         Phoenix           Technical Reference Manual        Page 133

              All  PATH fields will end with the  trailing  backslash,  
              reduces internal processing.

              E.g. C:\PHOENIX\MATRIX\

              If  you want to use one of the "unusedX" fields for  any  
              product  you  plan on releasing to the  general  public,  
              please  contact us to make sure it isn't being  used  by  
              something else.
              
              If  it  isn't,  we  will reserve  that  field  for  your  
              application.

                                   File Requests

              If  you  are  going to make any  type  of  "ROBOT"  file  
              request  program, you must BUILD that actual  .REQ  file  
              and ATTACH it to a message.

              Again,  Phoenix does NOT build the .REQ. It expects  the  
              application  to  take care of that. This allows  you  to  
              request  an  almost  unlimited number of  files  with  a  
              single request.

              Otherwise, you'd be limited to what you could squeeze on  
              the SUBJECT line of a message.