Ò  Ò  ÒÄ·  ÒÄ·  ÖÄÄ·
			    º  º  ÇÄÐ· ÇÄÐ· ÓÄÄ·
			     Ó½   ÐÄÄ½ ÐÄÄ½ ÓÄÄ½

	ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
		       *** VBBS MODEM DOCUMENTATION ***
	ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	Table of Contents

	I.    VCONFIG/Channel Configuration
	      A.  COM Port
	      B.  Base Address
	      C.  IRQ
	      D.  Baud Rate
	      E.  Init String
	      F.  Locked Baud Rate
	      G.  Hardware (RTS/CTS) Handshake
	      H.  Minimum Baud Allowed
	II.   UART Chips and Recommendations
	      A.  Reliability
	      B.  Multitasking
	III.  Modem Initialization Settings
	      A.  Modem AT Command Settings
	      B.  High Speed Modem Initialization Strings
	IV.   Discussion of Communications Standards
	      A.  Description of Standards
	      B.  Table of Modes
	      C.  Error Correction Standards
	      D.  Glossary of Terms
	V.    VBBS FOSSIL Documentation
	      A.  Number of Simultaneous Open Ports
	      B.  2 Node System
	      C.  4 Node System

	--------------------------------------------------------























					   VBBS Modem Documentation --  1

	 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	 º I.  VCONFIG/Channel Configuration                              º
	 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

		VBBS comes preconfigured to work correctly with most
	 2400 baud modems.  If you are setting up a 2400 baud system,
	 your modem configuration should be as simple as choosing the
	 correct modem port in VCONFIG's channel.cfg.  High speed
	 modems will probably require a more complex configuration.
	 Basic information is provided here for a sampler of those
	 modems.  Due to the variety of systems in use throughout the
	 network, indepth setup assistance for your specific hardware
	 is best obtained from the Modem Mania message base,
	 VirtualNET Sub #209.

		VBBS allows multiple phone lines to be configured,
	 depending on the registration level chosen.  For each data
	 line in VBBS, a channel (phone line) configuration must be
	 set to define the Serial COM port that the individual line(s)
	 will be running from.  An example follows:

		1.) COM Port :
		2.) Base Address (Hex):
		3.) IRQ (Hex) :
		4.) Baud Rate :
		5.) Init String :
		6.) Locked Baud Rate :
		7.) Hardware (RTS/CTS) Handshake :
		8.) Minimum Baud allowed :


	 A. COM Port
	 ÍÍÍÍÍÍÍÍÍÍÍ

	 Define a communications port for each channel in use.  COM
	 ports can be used more than once, but the repeated port must
	 have a different base address to prevent an IRQ conflict.

	 B. Base Address
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 The base address that DOS understands as the port assignment
	 for the channel. (example: COM1 is 3F8, COM2 is 2F8).

	 C. IRQ
	 ÍÍÍÍÍÍ

	 Assign an IRQ (Interrupt ReQuest) for further definition of 
	 the communications port.

	 D. Baud Rate
	 ÍÍÍÍÍÍÍÍÍÍÍÍ

	 Define your modem's baud rate speed, from 300 to 57600.

 








					   VBBS Modem Documentation --  2


	 E. Init String
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 The modem initialization string used by a particular channel
	 to define reset and operation of the modem.

	 F. Locked Baud Rate
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 Toggle YES/NO for locked baud rate at high speeds.  This
	 should be set to NO for 2400-baud and slower modems.

	 Note: High-speed modems should use a locked baud rate to
	 indicate the maximum throughput achieved by the modem.  For
	 instance, a 14400-baud modem could be defined as 14400, 19200,
	 38400, or 57600, as the modem allows.

	 G. Hardware (RTS/CTS) Handshake
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 Toggle "No, Yes(Normal), or Yes(Slow)".  This setting is for 
	 high speed modems.  Yes(Normal) is the preferred choice.

	 H. Minimum Baud Allowed
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 Configure a minimum speed to tailor a high-speed line.




































					   VBBS Modems Documentation --  3


	 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	 º II.  UART Chips and Recommendations                            º
	 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

		The NS16550AFN, or UART (Universal Asynchronous
	 Receiver/Transmitter) chip, is the heart of your asynchronous
	 communications board.  The advantage of the 16550 over the
	 16450 and 8250 UARTs is that it has a 16 byte buffer.


	 A.  Reliability

		On the older chips, with their single-byte buffer, 
	 you would lose data if a second byte came in from the modem
	 before the CPU had sufficient time to call the first byte.
	 The 16550, with its 16-byte buffer, gives the CPU up to 16
	 opportunities to access data before a character is lost.


	 B.  Multitasking

		When VBBS is transmitting data, it has to stop the 
	 CPU and fill the UART's transmit buffer.  That means that 
	 the background caller will experience a system slowdown while
	 VBBS attempts to send data to another caller.  In addition,
	 the older 8250 chips were much less reliable, and were never
	 designed for the high speeds of current modems.  The 
	 NS16550AFN, on the other hand, is designed with high bus 
	 speeds and high modem speeds in mind.  When multitasking, 
	 even at slower baud rates, the 16550 can be very helpful in
	 providing smooth operation for the entire system.
































					   VBBS Modems Documentation --  4


	 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	 º III.  Modem Initialization Settings                            º
	 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
	  
		Since high speed modems can utilize so many settings, 
	 it is almost impossible to include them all in one initiali-
	 zation string.  Therefore, you may wish to use the NRAM fea-
	 ture to store the settings which are common to most applica-
	 tions and use the VBBS init string for VBBS-specific settings.
		This collection of modem settings has been garnered 
	 over time from VBBS sysops working with an unlimited variety 
	 of hardware configurations.  If the following recommendations
	 provide unsatisfactory results, please refer to the VirtualNET
	 support subs for further assistance.


	 A.  Modem AT Command Settings
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 Standard 2400 bps or 1200 bps Hayes Compatibles (NON-MNP):

	 Supports the extended "&" command set:

		ATX4Q0E0V1&C1&D2S2=251S7=40

	
	 X4     Enables extended result codes
	 Q0     Modem returns result codes
	 E0     Modem does not echo commands back to the computer
	 V1     Modem returns verbal result codes
	 &C1    Modem asserts carrier detect based on connection
		status
	 &D2    On DTR high-to-low transition, modem Hangs Up.
	 S2=251 Disable modem escape sequence
	 S7=40  Time modem waits for a carrier when initiating a new
		connection

	
	 Does not support the extended "&" command set:
       
		ATX4Q0E0V1S2=251S7=40

	 Modems which do not use the & command set usually have DIP
	 switches of some type to set their mode of operation. Verify
	 that your modem is set to assert CD (carrier detect) only 
	 when connected to a remote modem and hang up on drop of DTR 
	 (data terminal ready).

	 
	 













					   VBBS Modems Documentation -- 5


	 B.  High Speed Modem Initialization Strings
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Aceex 14.4
								      
		AT&F1S0=0M0E0V1X4&C1&D2&M5\N0S95=1S46=136S36=5               

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
	
	 Boca 14.4 V32bis:

		AT&F E0 V1 Q0 W2 S95=3 S7=50 S0=0

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Compucom High Speed Modems:

		AT&F2*H1%C0\N0S25=2M0QV1ES11=50&C1&D2H&W

	 Compucom STAR:

		AT&F2*H2&D2S7=75&Y0&WX4M0L0S11=50


	 Recommendations:
		Assign the above values to NRAM settings, and the
	initialization string will actually read 

		ATZ0
	
	 To assign an NRAM setting, enter the above initialization
	 string, then type 

		AT&W0

	 To disable CCSP (Compucom proprietary protocol) type

		AT*H0
	  
	 Baud rate should be locked and set to 19200, or 38400 for
	 those with 16550 UARTs.

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Cardinal 9600:

		ATW2Q0V1E0&D2&C1S2=251M0&W2S95=1235

	 - or -

		ATQ0V1E0&D2&C1S2=251S7=45M0
	
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ








					   VBBS Modems Documentation --  6


	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Digicomm 14.4

		AT&F&C1*S1E0

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Lightning Communications:

		AT&FE0&D2&C1&Q9S7=65W2M0

		Locked Baud Rate:  38400
		RTS/CTS         :  Slow

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Motorola UDS 14.4 V32bis:

		AT&F E0 V1 Q0 S0=0 %R2 \Q3 \V1 \M0 &C1 &D2 \N7 S7=50

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 SupraFAXmodem 14.4 V32bis:

	       AT&F2 E0 V1 Q0 W2 S95=3 S7=50
	
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 TwinCom V.32:

	       ATE0H0M0Q0V1X4S0=0S2=1W0S95=145
	
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 US Robotics Courier HST / Courier Dual Standard:

	 NRAM Settings Recommended:

	 X7     Return full result codes
	 &H1    Turns on hardware handshaking for output from DTE (CTS
		line) *
	 &R2    Turns on hardware handshaking for input to DTE    (RTS
		line) *
	 &B1    Fixes the DTE to DCE rate **
	 &N0    Negotiates highest link rate with fallback/fallforward
		enabled
	 &M4    Enables ARQ if remote modem has ARQ
	 &C1    Modem asserts carrier detect based on connection
		status
	 &D2    On DTR high-to-low transition, modem hangs up
	 &A3    Give FULL EXTENDED Result Codes
 
	 (Choose one of the 3 &K commands below based on your preference)









					   VBBS Modems Documentation --  7


	 &K1    Enables data compression if remote modem requests
		compression
	 &K3    Enables V.42 bis data compression but not MNP5
	 &K0    Disables all compression
 
	 USRobotics Courier 14400 HST Dual Standard:
 
	 B0  C1  E1  F1  M1  Q0  V1  X7
	 BAUD=38400  PARITY=N  WORDLEN=8
	 DIAL=HUNT   ON HOOK   TIMER
 
	 &A3  &B1  &C1  &D2  &G0  &H1  &I0  &K3  &L0
	 &M4  &N0  &P0  &R2  &S0  &T5  &X0  &Y1  %R0
 
	 S00=000  S01=000  S02=251  S03=013  S04=010
	 S05=008  S06=002  S07=045  S08=002  S09=006
	 S10=007  S11=050  S12=050  S13=000  S14=000
	 S15=008  S16=000  S17=000  S18=000  S19=000
	 S20=000  S21=010  S22=017  S23=019  S24=150
	 S25=000  S26=000  S27=000  S28=008  S29=020
	 S30=000  S31=000  S32=001  S33=000  S34=000
	 S35=000  S36=000  S37=000  S38=000
 
	 - or -
 
	 B0  C1  E1  F1  M1  Q0  V1  X7
	 BAUD=19200  PARITY=N  WORDLEN=8
	 DIAL=HUNT   ON HOOK   TIMER
 
	 &A3  &B0  &C1  &D2  &G0  &H1  &I0  &K3  &L0
	 &M4  &N0  &P0  &R2  &S0  &T5  &X0  &Y1  %R0
 
	 S00=000  S01=000  S02=251  S03=013  S04=010
	 S05=008  S06=002  S07=045  S08=002  S09=006
	 S10=007  S11=070  S12=050  S13=000  S14=001
	 S15=008  S16=000  S17=000  S18=000  S19=000
	 S20=000  S21=010  S22=017  S23=019  S24=150
	 S25=000  S26=000  S27=000  S28=008  S29=020
	 S30=000  S31=000  S32=001  S33=000  S34=000
	 S35=000  S36=000  S37=000  S38=000

	 VBBS Initialization String:

		ATX7Q0E0V1S2=251S7=25&H1&R2&B1&M4&N0&K1&A3

	 - or -

		ATX7Q0E0V1S2=251S7=25&H1&R2&B1&A3

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ













					   VBBS Modems Documentation --  8


	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 USRobotics Courier 9600 HST Settings

	 C=1  E=1  F=1  M=3  Q=0  V=1  X=7  B=1
	 BAUD=19200  PARITY=N  WORDLEN=8
	 DIAL=TONE   ON HOOK    TIMER
 
	 &A1  &B1  &G0  &H1  &I2  &K0
	 &M4  &N0  &P0  &R2  &S1  &Y1
 
	 S00=000  S01=000  S02=251  S03=013
	 S04=010  S05=008  S06=002  S07=025
	 S08=002  S09=006  S10=007  S11=040
	 S12=050  S13=000  S14=001  S15=000
	 S16=000  S17=000  S18=000  S19=005
	 S20=000  S21=010  S22=017  S23=019
 
	 DIAL=TONE   M=3  X=7  F=1  B=1
	 BAUD=19200  PARITY=N  WORDLEN=8
 
	 &A1  &B1  &G0  &H1  &I2  &K0
	 &M4  &N0  &P0  &R2  &S1  &Y1
 
	 S02=251  S03=013  S04=010  S05=008
	 S06=002  S07=025  S08=002  S09=006
	 S10=007  S11=040  S12=050  S13=000
	 S15=000  S19=005  S21=010  S22=017
	 S23=019
 
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Additional USR Intitialization Strings:

	 USRobotics Dual Standard 14.4
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 (Square LEDs -- not the 16.8 model):

		AT&B1 B0 E0 V1 Q0 &N0 &M4 S7=50 &H1 &R2 &A3

	 (might work with newer 16.8 model also)


	 US Robotics HST 14.4
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 (Round LEDs -- reports CONNECT 9600 even if 14400):
 
		AT&B1 B1 E0 V1 Q0 &N0 &M4 S7=50 &H1 &R2 &A3













					   VBBS Modems Documentation --  9



	 Older US Robotics HST 9600
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		AT&B1 B1 E0 V1 Q0 &N0 &M4 S7=50 &H1 &R2


	 Also, another note: USRobotics modem users (Dual Std and
	 HST) can specify that a smaller transmit buffer should be
	 used during non-ARQ connections, so that when 2400/non-error
	 correcting callers call the board, the space-bar abort is
	 more responsive. The modem will auto-adjust the size of the
	 transmit buffer for each connection:

		non-ARQ: 128 bytes
		ARQ: 4k

	 To enable this modem feature, set S15=8.

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 Zoom 14400 Fax/Modem:

		Locked Baud Rate:  38400
		RTS/CTS         :  Slow

		AT&C1&D2E0H0Q0V1X4W0S95=3\T2

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	  Zoom 2400 V.42bis:

		ATX4Q0V1E0&D2&C1S2=251S7=45

	 ACTIVE PROFILE:

	 B1 E1 L2 M1 N1 P Q0 V1 W1 X4 Y0 &C0 &D0 &G0 &J0 &K3 &Q5 &R0
	 &S0 &T4 &X0 &Y0
	 S00:000 S01:000 S02:043 S03:013 S04:010 S05:008 S06:002
	 S07:045 S08:002 S09:006
	 S10:014 S11:095 S12:050 S18:000 S25:005 S26:001 S36:005
	 S37:000 S38:020 S44:003
	 S46:138 S48:000 S49:008 S50:255

	 STORED PROFILE 0:

	 B1 E1 L2 M1 N1 P Q0 V1 W0 X4 Y0 &C0 &D0 &G0 &J0 &K3 &Q5 &R0
	 &S0 &T4 &X0
	 S00:000 S02:043 S06:002 S07:030 S08:002 S09:006 S10:014
	 S11:095 S12:050 S18:000
	 S25:005 S26:001 S36:005 S37:000 S38:020 S44:003 S46:138
	 S48:007 S49:008 S50:255

	 STORED PROFILE 1:









					   VBBS Modems Documentation -- 10


	 B1 E1 L2 M1 N1 P Q0 V1 W0 X4 Y0 &C0 &D0 &G0 &J0 &K3 &Q5 &R0
	 &S0 &T4 &X0
	 S00:000 S02:043 S06:002 S07:030 S08:002 S09:006 S10:014
	 S11:095 S12:050 S18:000
	 S25:005 S26:001 S36:005 S37:000 S38:020 S44:003 S46:138
	 S48:007 S49:008 S50:255

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 ZyXEL High Speed:

	 This is saved as Profile 0.  Init string is just ATZ0.

	 Be aware that register S20 sets the DTE speed, set to 19200,
	 so you may want to change this to S20=2 or S20=1.

	 CURRENT SETTING:

	 B0   E0   L4   M0   N5   Q0   V1   X6
	 &B1  &C1  &D2  &G0  &H3  &J0  &K4  &L0  &M0  &N0  &P0  &R1
	 &S0  &X0  &Y0
	 *B0  *C0  *D0  *E0  *I0  *M0  *P9  *Q2  *S0

	 S00=000   S01=000   S02=251   S03=013   S04=010
	 S05=008   S06=003   S07=060   S08=002   S09=006
	 S10=007   S11=070   S12=000   S13=000   S14=002
	 S15=002   S16=000   S17=018   S18=000   S19=000
	 S20=003   S21=176   S22=000   S23=112   S24=133
	 S25=000   S26=000   S27=156   S28=064   S29=000
	 S30=000   S31=017   S32=019   S33=000   S34=030
	 S35=000   S36=000   S37=000   S38=016   S39=000

	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	 ZyXEL 14400 V.32 V.32bis V.42 V.42bis Send/Recieve Fax/Modem:

		AT&FX6E0&C1&D2&G2H0M0|

		Locked Baud: 19200
		Hardware handshaking normal
	
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ





















					   VBBS Modems Documentation -- 11


	 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	 º IV.   Discussion of Communications Standards                   º
	 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	 A.  Description of Standards
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 CCITT v.21       300 bps.  (FSK).
	 Bell  103J

	 Bell  202        1200 bps, half duplex.
	 Leased lines.

	 CCITT v.22       1200 bps. (DPSK).
	 Bell  212A

	 CCITT v.22bis    2400 bps. (DPSK).

	 CCITT v.26ter    2400 bps with echo cancellation

	 Bell  208        4800 bps. Used on leased lines.

	 CCITT v.27ter    G3 FAX at 4800 bps with fall back to 2400
			  bps.

	 CCITT v.29       G3 FAX at 9600 bps with fall back to 7200
			  and 4800 bps.  Also used by Compucom
			  modems.

	 CCITT v.32       9600 bps with echo cancellation.  Fall back
			  to 4800 bps.  Both directions simultaneously.
			  (QAM).
			     
	 CCITT v.32bis    14400 bps with echo cancellation.  Fall back
			  to 12000, 9600, and 7200 bps.  (TCM)  Both
			  directions simultaneously.

	 CCITT v.33       14400 with fall back to 12000 bps.
 
	 USR HST14400     US Robotics HST modulation.  14400 bps in
			  one direction and 450 bps in reverse
			  direction.  Fall back to 12000, 9600, and
			  4800 bps.

	 Trailblazer      Proprietary up to 18000 bps.

	 Hayes V-Series   Proprietary full-duplex 9600 baud.  Hayes'
			  CCITT LAP-B error correction and data
			  compression.

	 EIA Class2 FAX   G2 Fax standard.
 
	 CCITT v.FAST     19200 bps or slightly higher.  Uses echo
			  CCITT v.32bisbis.
 
	 ISDN             Integrated Services Digital Network on fiber
			  optic cable.
 
	 SMDS             Switched Multi-Megabit Data Service on fiber
			  optics.



					   VBBS Modems Documentation -- 12


	 HDSL             High-rate Digital Subscriber Link.  In
			  development.
 
	 
	 B.  Table of Modes
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 MODE          BPS       BAUD      MODULATION      NOTES
	 -------------------------------------------------------------
	 v.33         14400      2400       128-TCM
	 v.33         12000      2400        64-TCM
	 v.32bisbis   19200      2400       512-TCM
	 v.32bis      14400      2400       128-TCM
	 v.32bis      12000      2400        64-TCM
	 v.32bis       9600      2400        32-TCM
	 v.32bis       7200      2400        16-TCM
	 v.32          9600      2400        32-TCM
	 v.32          9600      2400        16-QAM        Uncoded
	 v.32          4800      2400         4-DPSK
	 v.29          9600      2400        16-QAM
	 v.29          7200      2400         8-QAM
	 v.29          4800      2400         4-DPSK
	 v.27ter       4800      1600         8-PSK
	 v.27ter       2400      1200         4-DPSK
	 G3 FAX                                            v.29/.27ter
	 v.22bis       2400       600        16-QAM
	 v.22          1200       600         4-DPSK       BELL 212A
	 ISDN         65536     65536        FiberOptic    Digital
 
	 The baud rate over the phone line means that more than two
	 tones are used at the baud frequency to achieve the bps rate.
	 For instance, 4-DPSK means four tones.
 

	 C.  Error Correction Standards
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 NAME      DESC OF ERROR CORRECTION AND DATA COMPRESSION
	 -------------------------------------------------------------
	 MNP1      Hardware error correction.
	 MNP2      Hardware error correction.
	 MNP3      Hardware error correction.  Strips off start and
		   stop bits during transmission over phone line.
	 MNP4      Hardware error correction.  Fastest way to send
		   compressed files.  Strips off start and stop bits
		   during transmission.  Also adapts to line
		   conditions.
	 MNP5      Hardware error correction and data compression (up
		   to 2 time compression on TEXT).  Do NOT use on
		   compressed files!
	 MNP6      Additional Universal Link Negotiation and
		   Statistical Duplexing to MNP5 service
	 MNP7      Additional Enhanced Data Compression with MNP4.
	 MNP8      TBA
	 MNP9      Additional Enhanced Data Compression with v.32
		   modems.  Also adds Enhanced Universal Link
		   Negotiation, which allows connection to both MNP
		   and non-MNP modems at the highest performance
		   level.
	 MNP10     Hardware error correction and data compression.



					   VBBS Modems Documentation -- 13


	 v.42      CCITT error correction. LAPM.  Fastest way to send
		   compressed files.  Strips off start and stop bits
		   during transmission.
	 v.42bis   CCITT data compression (up to 4 time compression on
		   TEXT).  Uses a version of the Lempel-Ziv data
		   compression algorithm.


	 D.  Glossary of Terms
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 baud        Actual rate of symbols trasmitted per second.
	 bps         Bits Per Second.
	 MNP         Microcom Networking Protocol.
	 CCITT       International Telephone and Telegraph
		      Consultative Committee.
	 FSK         Frequency Shift Keying.
	 DPSK        Phase Shift Keying.
	 QAM         Quadrature Amplitude Modulation.  Combination of
		      PSK and AM.
	 TCM         Trellis Coded Modulation.
	 LAPM        Link Access Procedure for Modems.
 








































					   VBBS Modems Documentation -- 14


	 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	 º V.    VBBS FOSSIL Documentation                                º
	 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

		The "standard" serial driver which comes with VBBS is not
	 able to allow IRQ sharing between COM ports.  This is not so
	 much a limitation in the driver, as a limitation of the
	 underlying operating environment.  A FOSSIL driver, on the
	 other hand, can handle 2 or more serial ports using the same
	 IRQ line.  In fact, a FOSSIL can be used to control up to 8
	 ports.  It can be "programmed" to use almost any serial board
	 in existence.

		VBBS has been extensively tested with both the BNU and X00
	 FOSSIL drivers. If you're new to FOSSIL drivers, they provide
	 a standard way for programs to communicate with serial ports.
	 The FOSSIL may load through either AUTOEXEC.BAT or CONFIG.SYS.  
	 The advantages and disadvantages of each are discussed at length 
	 within the individual FOSSIL documentation.


	 A.  Number of Simultaneous Open Ports
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 The basic CONFIG.SYS install for X00 is: DEVICE=X00.SYS

	 The basic AUTOEXEC.BAT install for BNU is: BNU

	 By default, a FOSSIL will assume you wish to have only one
	 communications port open at any given moment.  The FOSSIL
	 doesn't specify which port (COM1, COM2, COM3, etc) but is
	 merely concerned with the maximum number of simultaneous open
	 ports.  Each port you request is like a "data channel,"
	 corresponding to your VBBS data channels.  For more detailed
	 information on a driver, consult the specific FOSSIL
	 documentation.

	 B.  2-Node System
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 Channel 1 to be on COM1
	 Channel 2 to be on COM2
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		X00: DEVICE=X00.SYS 0=COM1 1=COM2
		BNU: BNU /P=2

		VCONFIG: Set Channel 1 to COM1
			 Set Channel 2 to COM2














					   VBBS Modems Documentation -- 15


	 Channel 1 to be on COM2
	 Channel 2 to be on COM3
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		X00: DEVICE=X00.SYS 0=COM2 1=COM3
		BNU: BNU /P=2

		VCONFIG: Set Channel 1 to COM2
			 Set Channel 2 to COM3



	 C.  4-Node System
	 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	 Channel 1 to be on COM1
	 Channel 2 to be on COM2
	 Channel 3 to be on COM3
	 Channel 4 to be on COM4
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		X00: DEVICE=X00.SYS 0=COM1 1=COM2 2=COM3 3=COM4
		BNU: BNU /P=4

		VCONFIG: Set Channel 1 to COM1
			 Set Channel 2 to COM2
			 Set Channel 3 to COM3
			 Set Channel 4 to COM4