ASYNCHRONOUS FUNCTIONS FOR MICROSOFT, TURBO, OR ZORTECH C


            The LIB(s) on the included disk are libraries of serial
         communications functions designed specifically for use with
         Microsoft C, Turbo C / C++, and Zortech C / C++.  The regis-
         tered version has LIBs for all memory models.  The shareware
         version is small model only.


                    --- Features of the library functions ---

            o Support for 16550 UART's FIFO mode of operation

            o Fully interrupt driven

            o Baud rates up to 115,200 baud

            o User defined transmit and receive ring buffer sizes.

            o Ring buffers may be in placed in FAR memory even in small
              and medium model programs.

            o User defined port addresses, IRQ use, and interrupt vector
              numbers.

            o Support for simultaneous operation of 4 ports.

            o Built in support for XON/XOFF and hardware flow control

            o Block transmit and receive functions

            o Receive buffer look ahead function

            o 100% assembler code for maximum speed

            o Totally compatible with Microsoft C, Turbo C, Zortech C,
              and other C compilers that use standard Microsoft high
              level language calling conventions.



         ---------------------------------------------------------------
                Mike Dumdei,  6 Holly Lane,  Texarkana TX  75503
                MCOMM5 (c) 1989, 1990, 1991  All Rights Reserved
         ---------------------------------------------------------------







                      REGISTRATION AND DISTRIBUTION POLICY

            MCOMM5, the various versions of Smalterm, the ANSI video
         routines, and other miscellaneous functions contained in the
         COMM_x libraries are distributed as shareware.  If you use
         these functions regularly please register them.

            Two types of registration are available for MCOMM5.  The
         first is $25 and includes assembled libraries for all memory
         models.  The $25 registration does not include source code.
         The second type of registration is $45 and includes libraries
         and source code.  Previous versions were $25 for source code
         and libraries.  If you send $25 and want source code based on
         previous offers, you will receive a previous version of the
         source.  Registered users of versions prior to version 5 may
         upgrade their libraries for $3 or upgrade source code version
         for $10.

            Considerable time and effort has gone into developing and
         debugging these routines.  If you are not a registered user and
         have obtained a copy of the registered version, please take
         time now to register the software or delete it.  The copy you
         have is a registered version if it contains libraries for any
         memory model other than small model or if any of the ASM source
         code is included.

            This software is provided as is without warranty as to its
         fitness for a particular use or being free of errors.  I assume
         no liability for any loss or damages you may incur through its
         use.  I will, however, make every effort to correct any
         software errors that may exist, and provide you with a working
         version.

            I will continue to assist registered and non-registered
         users whenever possible.  If you have any problems using these
         routines or questions, I may be contacted at:

            North East Texas DataLink --  903 838-6713 (modem)
                                          FIDO net:  1:3819/128

            Mike Dumdei               --  903 838-8307 (voice)







                                 GETTING STARTED

         All functions included in this library are listed on the fol-
         lowing pages in alphabetical order.  The basic functions needed
         to begin are: async_open, async_tx, async_rx, and async_close.

         Functions are also available to support XON/XOFF and hardware
         flow control, the 16550 UART, block transmit and receive,
         receive buffer look ahead, and several other features.

         All functions take a pointer to an ASYNC structure for one of
         its arguments.  This structure is defined in COMM.H.  It
         may be helpful to think of this structure as being similar to
         the standard C library 'FILE *'.

         If you have been using versions of these routines prior to
         version 5.00, there have been some changes made that will
          require you to make some modifications to any existing code
         before it can be used with the new libraries.  The main
         differences are:

            > Async_open takes different parameters.  Also, instead
              of the open function automatically allocating the ring
              buffers for you, you provide the ring buffers.

            > All functions now take a pointer to an ASYNC structure
              as the first argument rather than 0 (COM1) or 1 (COM2).

            > LITES is no longer supported.







                            NOTES ON 16550 FIFO MODE

            The 16550 UART is automatically detected and enabled when
         async_open is called.  If, for some reason, you want to operate
         a 16550 UART in non-FIFO mode, automatic detection and use can
         be disabled.  See async_open for more information.


                          --- Use of receiver FIFOs ---

            The receiver trigger level may be programmed for 1, 4, 8, or
         14 bytes by the async_FIFOrxlvl function.  When a port is first
         opened the trigger is set to 1 byte.  There are 3 reasons why I
         chose to default to a 1 byte receive trigger level.

            1) While a higher trigger level results in less CPU
               overhead, it also provides less overrun protection if the
               CPU is slow to respond.  For example, with a 1 byte
               trigger level the 16550 -- when it generates an interrupt
               -- can hold 15 more characters in its FIFOs before the
               CPU responds.  With a 14 byte trigger level it will only
               have room for 2 more characters.

            2) The MCOMM interrupt functions completely empty the
               receiver FIFOs every time an interrupt occurs.  If the
               CPU is slow to respond, the interrupt handler will
               process 2,3,4.. characters (whatever is in the FIFOs)
               whenever it does get control so the data still gets
               buffered if the CPU isn't able to keep up.

            3) Setting the trigger level at higher trigger levels when
               displaying incoming data to the screen will result in a
               jerky looking display, especially at low baud rates.
               Again, this is because MCOMM empties the buffer
               completely when it processes the interrupt.  With a
               trigger level other than 1, data stacks up in the FIFOs
               until the trigger level is reached.  When the interrupt
               finally occurs, all the data in the FIFOs is pulled out
               and made available to the higher level functions at
               one time.  The result is your code sits for 4, 8, or 14
               bytes (whatever the trigger is) and then puts those bytes
               on the screen in a burst.  It looks rough at low baud
               rates.  At 9600 baud and above you could probably get by
               with a slightly higher trigger level.

            For best use of the receive FIFOs, stick with 1 byte trigger
         level when displaying data to the screen.  If your application
         does not display the data or uses a high baud rate, you may
         want to experiment with setting it to either 4 or 8 bytes.


                          --- Use of transmit FIFOs ---

            The MCOMM transmit interrupt handler takes a parameter (set
         by async_FIFOtxlvl) that is the maximum number of bytes to load
         into the transmit FIFOs at one time.  The default value for







                            NOTES ON 16550 FIFO MODE

         this parameter is 3 bytes.  The reason for not loading up the
         FIFOs to maximum capacity (16 bytes) is flow control.  The
         16550 UART will continue to transmit characters in its FIFOs
         regardless of the state of CTS, DSR, or CD, or if an XOFF is
         received.  It is totally up to the software to respond to
         requests for flow control.  If the FIFOs are loaded with more
         bytes than the receiver can handle when it invokes flow
         control, the receiver gets overwritten.  There is a bit that
         can be sent to the UART to flush the transmit FIFOs but then it
         is impossible to tell what was flushed and what was sent.  The
         solution is to not the load the FIFOs up so full.  If the
         receiving device can handle more than 3 characters of overrun,
         use a larger value.  If the application does not require flow
         control, you can use a 16 byte level with no problems.

            Another factor to consider concerning the transmit FIFO byte
         level is that (from the NS Data Communications/LAN/UART
         Handbook) the transmit FIFO empty indication will be delayed by
         1 character time minus the last stop bit until there are at
         least 2 bytes in the transmit FIFOs simultaneously for the
         current transmit operation.  After the 2 byte requirement is
         met the transmit interrupt occurs immediately when the transmit
         FIFOs empty.  Using a value of 3 or above (1 byte for the
         transmit shift register and 2 for the FIFO registers)
         guarantees the interrupt delay is deactivated.  Once the '2
         bytes in the FIFOs' requirement is met, the transmit byte level
         can be reduced if necessary.


                  --- Problems with Western Digital 16550s ---

         The following problems DO NOT apply to the National Semicon-
         ductor version of the 16550.  Neither are they unique to MCOMM.

         Western Digital 16550 UARTs have two problems you should be
         aware of if your application will be ran on system that uses
         this chip.

         The first of these only shows up under the following
         conditions:

            1) The UART is in FIFO mode.
            2) A low baud rate is being used.
            3) The transmitter is initially empty.
            4) A block of data longer than 16 to 18 bytes (depth of the
               FIFOs plus 1 or 2 for what gets out while the FIFOs are
               being filled up) is sent to the chip.

         Under these conditions the WD16550 UART will momentarily fail
         to recognize the FIFOs are full and continue to generate
         transmit interrupts.  It also fails to reset the 'Transmit Hold
         Register Empty' bit making it impossible for the software to
         detect a full FIFO condition.  The result is the software keeps
         sending data to the chip, overrunning the FIFOs.  What you will







                            NOTES ON 16550 FIFO MODE

         see is, the first 16 to 18 bytes transmitted correctly, a
         missing block of data, and then the remainder of the block also
         correct.  This can be verified by trying to send blocks of data
         through this chip (WD16550) at a low baud rate with any
         software that enables the FIFOs.  How low of a baud rate is low
         enough to cause the problem depends on the particular chip and
         how fast the CPU and software can supply data to the chip.
         With MCOMM, a 20 MHZ 386, and the TxByteCnt at the default
         level of 3, the chip I was testing would not work in FIFO mode
         below 9600 baud.  On the same system using different software,
         it worked as low as 4800 baud.  On a 12 MHZ 286, MCOMM would
         work at 4800 and above while the other software worked at 2400
         and above.

         For publicly distributed applications, I recommend you do one
         or more of the following:

            1) Provide an option in your program to allow the end user
               to operate a 16550 with the FIFOs disabled.  When the
               FIFOs are disabled, all baud rates work.  ORing the
               'vctrnbr' parameter of async_open with 0x4000 will force
               FIFO mode off.
            2) Provide an option in your program to allow setting the
               TxByteCnt level (async_FIFOtxlvl) to a lower value.  This
               will help slightly.

            3) Put a flag in your program the end user can set to let
               you know you are dealing with a WD16550.

            4) State your application does not support the Western
               Digital version of the 16550 at low baud rates.


         The second problem with the WD16550 is that if the 'Clear to
         Send' signal is not connected it can, under some conditions,
         cause the 'Delta Clear to Send' bit in the Modem Status
         Register to become set and it will not reset.  I did not
         research the problem enough to know if the 'locked bit' only
         occurs when MSR interrupts are enabled, whether other floating
         MSR input signals can cause the same problem, if all WD16550's
         have the problem, or that is unique to the Western Digital chip
         (considering the FIFO overrun problem, I assume it is unique).

         With a properly functioning UART, reading the MSR register will
         reset all the 'delta bits' and clear any interrupts.  With the
         chip I had, I tried everything I could think of to clear the
         interrupt and nothing worked except the ON/OFF switch.  I tried
         clearing interrupts and reading the MSR multiple times checking
         to see if the bit reset with interrupts off (it didn't),
         disabling Modem Status interrupts via the Interrupt Enable
         Register and then reading the MSR register (didn't work), FIFO
         mode on / FIFO mode off (no difference), keyboard reboot of the
         computer (didn't fix it), shut the computer off and turn it
         back on (that fixed it).







                            NOTES ON 16550 FIFO MODE

         After encountering this problem and having the system lock up,
         I added code to MCOMM's interrupt driver so that it would quit
         trying to clear an interrupt after 1000 attempts.  It then sets
         a new port structure member 'IERVal' to zero as an indicator
         the port is locked up.  Normally 'IERVal' will be set to the
         current value of the Interrupt Enable Register.  If you try to
         open a port that is in a stuck interrupt condition, async_open
         now returns R_UARTERR.  In addition, options were added to open
         a port without enabling Modem Status interrupts or Line Status
         interrupts or both.  ORing the 'vctrnbr' parameter of async_open
         with 0x2000 disables MSR interrupts.  ORing with 0x1000
         disables LSR interrupts.  So far I have encountered no reason
         for disabling LSR interrupts.  Disabling MSR interrupts
         prevents the lock up problem but has the side effect of causing
         all functions and variables that use Modem Status signals to be
         invalid.  This includes hardware handshake and carrier detect.

         I have probably over emphasized the Modem Status lock up
         problem and my personal opinion is that it is not that serious.
         I considered totally disregarding it since it has a simple
         solution and that is to connect all Modem Status input signals
         to some driving signal (wire the RS232 cable right).  Unused
         signals can be connected to a driving signal on the computer
         end if necessary.  Also it may be isolated to one defective
         chip.  I tested two WD16550s and the problem only showed up on
         one of them during my testing.  Because the computer totally
         locked up when this happened though, I decided to go ahead and
         program for the possibility.  At least control of the computer
         is regained and you can tell the user he needs a properly wired
         RS232 cable or his UART is broke and then exit gracefully.
         This will probably show up very very rarely so don't be too
         concerned about it.  In closing, I would like to point out
         again that these problems are a fault of the WD16550 and are
         not unique to MCOMM.







         async_16550
         ---------------------------------------------------------------

         Purpose: Check if 16550 UART was detected in system.

         Format:  int async_16550(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int is_16550;

                  is_16550 = async_16550(port);

         Returns: Returns zero if a 16550 is not in the system or the
                  'ignore 16550 bit' was set when async_open was called.
                  Returns NZ if a 16550 was found.  Async_open must be
                  called before this function is valid.  If a 16550 is
                  found, it will be placed in the FIFO mode of operation
                  by async_open unless '16550 detect' was overridden or
                  the force FIFOs off option was selected.

         Remarks: This function is implemented as a macro.

                  See async_open.







         async_breakrxd
         ---------------------------------------------------------------

         Purpose: Checks if a break signal has been received.

         Format:  int async_breakrxd(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int break_status;

                  break_status = async_breakrxd(port);


         Returns: If a break signal has been received the function
                  returns a non-zero value.  If a break has not been
                  detected, zero is returned.

         Remarks: Once a break signal has been detected, this function
                  continually returns non-zero values until async_reset
                  is called.  If a break is received, a line status
                  register interrupt is generated.  The interrupt
                  handler sets a bit in the Stat1 port structure member.
                  The async_breakrxd function is a macro that checks the
                  status of this bit.

                  See also async_reset, async_rx, async_stat,
                  async_sndbrk.







         async_carrier
         ---------------------------------------------------------------

         Purpose: Check for the presence of a carrier.

         Format:  int async_carrier(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int carrier_status;

                  carrier_status = async_carrier(port);


         Returns: A non-zero value is returned if a carrier is present.
                  If the carrier detect line is LOW, zero is returned.

         Remarks: This function is implemented as a macro.  See also
                  async_rx and async_stat.







         async_close
         ---------------------------------------------------------------

         Purpose: Closes a port opened by async_open.

         Format:  int async_close(port);
                   ASYNC *port;    Pointer to ASYNC structure

         Example:

                  ASYNC port;
                  async_close(&port);

         Returns: No return value

         Remarks: Do not attempt to close an unopened port.  Some
                  minimal checking is done internally by async_close in
                  an attempt to detect whether or not the specified port
                  is actually opened.  If an unopened port makes it past
                  those checks and the main close routine is entered,
                  the system may lock up (immediately, 2 hours later, or
                  never).  When a port is closed the UART registers,
                  interrupt controller mask, and interrupt vectors are
                  restored to the value they had when async_open was
                  called.  It is possible to close the port and leave
                  various signals (DTR for one) in the state you desire
                  rather than in their initial state.  See async_dtr and
                  async_rts for some examples on how to do this.

                  The B_ORGFIFO bit in the ASYNC 'Stat3' structure
                  member is used by async_close to return the 16550 --
                  if present -- to the mode it was in when async_open
                  was called.  FIFOs may be 'forced' to remain enabled
                  or 'forced' to be disabled when closing the port by
                  first setting or resetting this bit.  Ex:

                    Force off:    port->Stat3 &= ~B_ORGFIFO;
                                  async_close(port);

                    Force on:     port->Stat3 |= B_ORGFIFO;
                                  async_close(port);







         async_cts
         ---------------------------------------------------------------

         Purpose: Check status of the Clear to Send signal.

         Format:  int async_cts(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int cts_status;

                  cts_status = async_cts(port);

         Returns: Returns zero if Clear To Send is LOW.  If CTS is HIGH,
                  a non-zero value is returned.

         Remarks: This function is implemented as a macro.







         async_dsr
         ---------------------------------------------------------------

         Purpose: Check status of the Data Set Ready signal.

         Format:  int async_dsr(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int dsr_status;

                  dsr_status = async_dsr(port);

         Returns: Returns zero if Data Set Ready is LOW.  If DSR is
                  HIGH, a non-zero value is returned.

         Remarks: This function is implemented as a macro.







         async_dtr
         ---------------------------------------------------------------

         Purpose: Set or reset the Data Terminal Ready signal.

         Format:  void async_dtr(port, DTRflag);
                   ASYNC *port;       Pointer to ASYNC structure
                   int DTRflag;       Set/Reset DTR flag

         Example:

                  ASYNC *port;

                  if (WantToDropDTR)
                      async_dtr(port, 0);
                  else if (WantDTRhigh)
                      async_dtr(port, 1);


         Returns: No return value

         Remarks: This signal is set HIGH when a port is first opened.
                  When the port is closed, it is restored to the cond-
                  ition it was in when the port was opened.  To force
                  DTR low when a port is closed, regardless of its state
                  when the port was opened, AND the port member, OldMCR,
                  with NOT B_DTR.  To force DTR to remain high when the
                  port is closed, OR OldMCR with B_DTR.

                    Force low:    port->OldMCR &= ~B_DTR;
                                  async_close(port);

                    Force high:   port->OldMCR |= B_DTR;
                                  async_close(port);







         async_FIFOrxlvl  <5.20 addition>
         ---------------------------------------------------------------

         Purpose: Set the 16550 UART's receive trigger level.

         Format:  void async_FIFOrxlvl(port, trigger_lvl);
                   ASYNC *port;       Pointer to ASYNC structure
                   int trigger_lvl;   Rx FIFO interrupt trigger level

         Example:

                  ASYNC *port;

                   /* set the receiver trigger level to 8 bytes */
                  async_FIFOrxlvl(port, 8);

         Returns: No return value

         Remarks: Valid values for 'trigger_lvl' are 1, 4, 8, and 14
                  bytes.  When a port with a 16550 UART is first opened,
                  the trigger level is set to 1 byte.  See the
                  discussion on 'Use of receiver FIFOs' at the beginning
                  of this document.  This function has no effect if the
                  FIFOs were not enabled when async_open was called.







         async_FIFOtxlvl  <5.20 addition>
         ---------------------------------------------------------------

         Purpose: Set the number of bytes loaded into the 16550 UART's
                  transmit FIFOs when a transmit interrupt occurs.

         Format:  void async_FIFOtxlvl(port, bytes);
                   ASYNC *port;       Pointer to ASYNC structure
                   int bytes;         # of bytes to load into tx FIFOs

         Example:

                  ASYNC *port;

                   /* set the transmit FIFO byte level to 16 bytes */
                  async_FIFOrxlvl(port, 16);

         Returns: No return value

         Remarks: Valid values for 'bytes' are 1 through 16 bytes.  When
                  a port with a 16550 UART is first opened, the transmit
                  level byte count is set to 3 bytes.  See the
                  discussion on 'Use of transmit FIFOs' at the beginning
                  of this document.  This function has no effect if the
                  FIFOs were not enabled when async_open was called.







         async_ignerr
         ---------------------------------------------------------------

         Purpose: Set or reset 'ignore characters with errors' bit

         Format:  void async_ignerr(port, flag);
                   ASYNC *port;       Pointer to ASYNC structure
                   int flag;          Set/Reset flag

         Example:

                  ASYNC *port;

                  if (WantToDiscardErrChars)
                      async_ignerr(port, 1);
                  else if (WantToKeepErrChars)
                      async_ignerr(port, 0);


         Returns: No return value

         Remarks: This function sets the bit that determines what hap-
                  pens to received characters that have parity or fram-
                  ing errors.  If the function is called with the flag
                  set to one, incoming characters that have framing or
                  parity errors are discarded -- they do not get put
                  into the receive ring buffer.  If the flag is 0, char-
                  acters with errors are not ignored, they are put into
                  the ring buffer.  The error bits in Stat1 that reflect
                  these error conditions are set regardless of the
                  setting of the discard flag.  When a port is first
                  opened, the flag is set to 0.  This function is imple-
                  mented as a macro.

                  See also async_stat.







         async_msr
         ---------------------------------------------------------------

         Purpose: Get the contents of the Modem Status Register.

         Format:  int async_msr(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int MSRcontents;

                  MSRcontents = async_msr(port);


         Returns: The contents of the Modem Status Register.

         Remarks: This function is a macro that returns the port struc-
                  ture member, MSRVal.  This value is initialized when a
                  port is first opened and then updated any time a modem
                  status interrupt occurs.  The reason the MSR is not
                  read directly is to avoid inadvertently intercepting a
                  pending MSR interrupt.  All bits returned except for
                  the delta bits reflect the true current status.







         async_msrflow  <5.50 modified>
         ---------------------------------------------------------------

         Purpose: Enables or disables hardware flow control.

         Format:  void async_msrflow(port, flowmask);
                   ASYNC *port;       Pointer to ASYNC structure
                   int flowmask;      Bit mapped flow control mask

         Example:

                  ASYNC *port;

                  if (enable_RTS_CTS_handshake)
                      async_msrflow(port, B_CTS);
                  else if (disable_handshake)
                      async_msrflow(port, 0);

         Returns: No return value

         Remarks: The flow mask is a bit mapped value of the signal that
                  is monitored by the receiver when performing flow
                  control.  Bits that may be monitored are B_CTS, B_DSR,
                  and B_CD.  This provides capability for RTS/CTS hand-
                  shake, DTR/DSR handshake, and handshaking with the
                  carrier detect line.  To monitor multiple signals, OR
                  the bits together.  Both hardware flow control and
                  XON/XOFF flow control may be enabled at the same time.

                  Beginning with version 5.50, ORing B_RTS into the
                  'flowmask' parameter, will cause the RTS signal to be
                  driven low whenever the receive buffer exceeds the
                  XoffTrip point.  RTS will automatically return to its
                  normal condition when the receive buffer empties to a
                  point below the XonTrip level.  Both XOFF/XON and RTS
                  flow control share the same trip point variable but
                  may be activated separately or together.  Do not get
                  RTS and CTS confused.  Use CTS to keep the computer
                  from overrunning a device (e.g. sending to a modem
                  with a locked baud rate).  Use RTS to keep from
                  getting ran over by a device (receiving from a high
                  speed modem using a slow computer).

                  See async_xflow.







         async_open  <5.40 modified -- see Remarks at end of function>
         ---------------------------------------------------------------

         Purpose: Initializes the hardware, interrupt vector, and ASYNC
                  port structure for interrupt driven operation.

         Format:
                  int async_open(port, base, irqmask, vctrnbr, params);
                   ASYNC *port;   Pointer to ASYNC structure
                   int base;      Base port address of UART chip
                   int irqmask;   8259 mask value for selected IRQ line
                   int vctrnbr;   Number of selected interrupt vector
                   char *params;  Baud, parity, data, & stop bits in
                                   string format

         Entry:   Before calling this function you must allocate ring
                  buffer memory and pre-initialize the following ASYNC
                  structure members:

                   RxSize : the size that you want the receive ring
                      buffer to be.  The memory allocated or set aside
                      for the receive ring buffer must be contiguous
                      with the memory used for the transmit  ring
                      buffer.  In most cases (RxSize + TxSize) bytes
                      will be allocated using some form of malloc.
                      A function to do this is included in the examples.
                      The combined size of RxSize + TxSize can not
                      exceed 32K - 1.

                   TxSize : the size of the transmit buffer in bytes.
                      As stated above, the transmit and receive buffers
                      for each individual port must be allocated as one
                      contiguous block.

                   RingSeg: the segment address of the memory allocated
                      for the receive and transmit buffers.  FAR memory
                      can be used for the receive and transmit buffers
                      by using your compiler library's version of FAR
                      malloc and putting the segment portion (high 16
                      bits) of the returned memory pointer in RingSeg.
                      If you are using a NEAR data model program and
                      want NEAR ring buffers, set RingSeg equal to 0.
                      With RingSeg set to zero, the open function will
                      use the DS segment register for RingSeg.  Using
                      FAR ring buffers causes no loss of performance.

                  RingOfst: the offset address of the memory allocated
                      for the receive and transmit buffers.  This value,
                      in conjunction with the RxSize and TxSize vari-
                      ables, is used to set up the receive and transmit
                      ring buffers.







         async_open
         ---------------------------------------------------------------

                  THE FOLLOWING FUNCTION IS INCLUDED WITH MCOMM5 AND IS
                  RECOMMENDED FOR ALLOCATING RING BUFFER MEMORY AND
                  INITIALIZING THE ABOVE VARIABLES.

         #if defined (__TURBOC__)         /* Turbo C */
            #include <alloc.h>
            #define _fmalloc farmalloc
         #elif defined (__ZTC__)          /* Zortech C */
            #include <dos.h>
            #include <stdlib.h>
            #define _fmalloc farmalloc
         #else                            /* Microsoft C */
            #include <malloc.h>
         #endif

         int AllocRingBuffer(
          ASYNC *port,                  /* pointer to port structure */
          int rxsize,      /* number bytes to use for receive buffer */
          int txsize,     /* number bytes to use for transmit buffer */
          int useFARmem)    /* flag set if using FAR mem for buffers */
         {
            unsigned long memptr;
            int memsize;

            memsize = rxsize + txsize;

            if (useFARmem || sizeof(char *) == 4)/* if FAR Ring bufs */
               memptr = (unsigned long)_fmalloc(memsize);
            else                  /* if Ring buffers use NEAR memory */
               memptr = (unsigned long)(unsigned int)malloc(memsize);

             /* pre-initialize 4 required structure members */
            port->RxSize = rxsize;            /* receive buffer size */
            port->TxSize = txsize;           /* transmit buffer size */
            port->RingSeg = (int)(memptr >> 16);          /* SEG adr */
            port->RingOfst = (int)memptr;            /* OFST address */
            if (memptr == 0L)
               return 0;          /* return 0 if no memory available */
            return 1;                   /* return 1, had some memory */
         }







         async_open
         ---------------------------------------------------------------

         Example 1:

            /*
               Open COM1 at 2400,N,8,1 using FAR ring buffers. COM1 is
               defined in COMM.H as:  0x3f8, 0x10, 12.  It is not
               necessary to check the return value of AllocRingBuffer
               since async_open will return R_NOMEM if the memory
               allocation function fails.
            */

            #include "comm.h"

            ASYNC port;
            int rcode;

            AllocRingBuffer(&port, 24000, 8000, 1);

            rcode = async_open(&port, COM1, "2400N81");
          /**  or
            rcode = async_open(&port, 0x3f8, 0x10, 12, "2400N81");
           **  or
            rcode = async_open(&port, 0x3f8, IRQ4, VCTR4, "2400N81");
           **/

            if (rcode != R_OK)
            {
                printf("\nAsync_open failed, exit code = %d", rcode);
                exit(rcode);
            }







         async_open
         ---------------------------------------------------------------

         Example 2:

            /*
               Open a port located at 0x2e0 that uses IRQ3.  In this
               case NEAR ring buffers are specified and the memory for
               the port structure is obtained using malloc.  See the
               AllocRingBuffer function described previously.
            */

            #include "comm.h"

            ASYNC *port;
            int rcode;

            if ((port = (ASYNC *)malloc(sizeof ASYNC)) == NULL)
            {
                printf("\nNot enough memory");
                exit(R_NOMEM);
            }

            AllocRingBuffer(port, 4096, 1200, 0);

            rcode = async_open(port, 0x2e0, IRQ3, VCTR3, "115200E71");

            if (rcode != R_OK)
            {
                printf("\nAsync_open failed, exit code = %d", rcode);
                exit(rcode);
            }







         async_open
         ---------------------------------------------------------------

         Example 3:

            /*
               Open both COM1 and COM2 at the same time.  You can open
               four ports at once as long as they don't share the same
               port addresses, IRQ lines, or interrupt vectors.
            */

            #include "comm.h"

            ASYNC ports[2], *port[2];
            int rcode;

            port[0] = &ports[0], port[1] = &ports[1];

            AllocRingBuffer(port[0], 10240, 10240, 1);
            rcode = async_open(port[0], COM1, "9600N81");
            if (rcode != R_OK)
            {
                printf("\nAsync_open failed, exit code = %d", rcode);
                exit(rcode);
            }

            AllocRingBuffer(port[1], 10240, 10240, 1);
            rcode = async_open(port[1], COM2, "1200E71");
            if (rcode != R_OK)
            {
                printf("\nAsync_open failed, exit code = %d", rcode);
                exit(rcode);
            }







         async_open
         ---------------------------------------------------------------

         Example 4:

            /*
               Open COM1 using its current baud, parity, data, and
               stop bit settings.  The port structure member, BPDSstr,
               will reflect those settings after calling async_open.
            */

            #include "comm.h"

            ASYNC *port;
            int rcode;

             /* alloc port structure & ring buffer memory */
            port = malloc(sizeof(ASYNC));
            AllocRingBuffer(port, 4096, 2048, 1);

             /* empty parameter string causes port to be opened at
                its current settings  */
            rcode = async_open(port, COM1, "");

            if (rcode != R_OK)
            {
                printf("\nAsync_open failed, exit code = %d", rcode);
                exit(rcode);
            }

            printf(
             "\nBaud, parity, data, stop bits = %s\n", port->BPDSstr);







         async_open
         ---------------------------------------------------------------

         Returns:

                  R_OK (0) - the port was opened with no errors.

                  R_NOMEM - a NULL pointer was passed as the address
                      of the ring buffers.  Probable causes are either
                      failing to initialize the port structure ring
                      buffer variables or assigning the RingSeg and
                      RingOfst structure a NULL pointer.  This could
                      occur if you use the AllocRingBuffer function or
                      something similar and the call to malloc fails.

                  R_BAUDERR - the passed baud rate in the BPDS string
                      was invalid.  Some possible reasons for this error
                      are leading spaces in the parameter string or use
                      of commas.  "115200N81" is correct. " 115200N81"
                      and "115,200N81" are both incorrect.

                  R_PARITYERR - an invalid character was found in the
                      parameter string where the parity should have
                      been.  Commas or spaces in the parameter string
                      are possible causes.  Valid parity settings are N
                      - none, E - even, or O - odd.  See R_BAUDERR.

                  R_DTABITERR - an invalid number of data bits was spec-
                      ified.  Only settings of 7 or 8 are supported.

                  R_STPBITERR - an invalid number of stop bits was spec-
                      ified.  Stop bits must be set to either 1 or 2.

                  R_IRQUSED - an attempt was made to open two ports that
                      use the same IRQ line.

                  R_VCTRUSED - an attempt was made to open two ports
                      that use the same interrupt vector.

                  R_NOPORT - an attempt was made to open more than four
                      simultaneous ports.

                  R_PORTUSED - an attempt was made to open two ports
                      that have the same I/O address.

                  R_UARTERR - an attempt was made to open a port that is
                      stuck in an interrupt condition (see the notes on
                      problems with the WD16550 at the beginning of this
                      documentation ).







         async_open
         ---------------------------------------------------------------

         Remarks (16550 support):

                  This function now automatically detects the presence
                  of a 16550 UART and enables FIFO operation if one is
                  detected.  By ORing either 0x8000 or 0x4000 with the
                  'vctrnbr' argument, you can change the default of auto-
                  enabling FIFO mode.  If 0x8000 is ORed with the
                  'vctrnbr' argument (ex: 0x8000|vctrnbr), no attempt is
                  made to detect a 16550 and no changes are made to the
                  mode of operation of the 16550 if one is present.  If
                  this bit is set, none of the functions or bits
                  relating to the 16550 UART will be valid.  If 0x4000
                  is ORed with the 'vctrnbr', the 16550 will be forced
                  into non-FIFO mode.

                  ORing 0x2000 with the 'vctrnbr' parameter will open the
                  port with MSR interrupts disabled.  ORing the 'vctrnbr'
                  parameter with 0x1000 will open the port with LSR
                  interrupts disabled.  See the notes on the WD16550 at
                  the beginning of this documentation for why this may
                  be desired and the side effects of opening a port with
                  MSR interrupts disabled.

                  When async_open is called, the FIFOs are momentarily
                  disabled and then re-enabled with the receive trigger
                  level set to 1 byte.  In versions of MCOMM prior to
                  5.40, the FIFOs were not reset if they were already
                  on.  Resetting the FIFOs was added to correct
                  occasional rare problems with the port not opening.

                    /* detect 16550, enable FIFOs if present */
                  async_open(PortPtr, 0x3f8, IRQ, Vector, Params);

                   /* do not attempt to detect 16550 */
                  async_open(PortPtr, 0x3f8, IRQ, 0x8000|Vctr, Params);

                   /* detect 16550, disable FIFOs if present */
                  async_open(PortPtr, 0x3f8, IRQ, 0x4000|Vctr, Params);

                   /* open port, disable MSR interrupts */
                  async_open(PortPtr, 0x3f8, IRQ, 0x2000|Vctr, Params);

                   /* open port, disable MSR interrupts and FIFOs */
                  async_open(PortPtr, 0x3f8, IRQ, 0x6000|Vctr, Params);







         async_open
         ---------------------------------------------------------------

         Remarks (versions previous to 5.00):

                  There are some major differences in the async_open
                  function in MCOMM5 and previous versions of the rou-
                  tines.  The two most major ones are that the parame-
                  ters passed to the function are different and it is
                  now necessary to allocate the memory for the ring
                  buffers before calling the function.  To make things
                  simpler, COM1 and COM2 are defined in COMM.H and the
                  function, AllocRingBuffer, is provided.  The COM1 and
                  COM2 definitions satisfy the requirements for the 2nd,
                  3rd, and 4th parameters required by the function.  For
                  ports other than the standard COM1 and COM2, it is
                  necessary to list the individual arguments.  The func-
                  tion, AllocRingBuffer, is provided in C source form on
                  the disk and included in the COMM_x libraries.  This
                  function allocates the ring buffer memory and initial-
                  izes the required port structure members.

                  The return values for async_open are different and may
                  have a different meaning than in earlier versions.

                  If a port is opened with an empty parameter string
                  (using "" for the parameters), then the port is opened
                  at its current settings and the port member BPDSstr is
                  set to the string representation of those values.

                  Async_open no longer checks the BIOS ram area at 40:0
                  to verify that a port actually exists.  There were too
                  many compatibles that did not store the proper values
                  there.

                  The maximum combined size of the receive and transmit
                  buffers for each port is 32K - 1.

                  FAR ring buffers in small and medium memory model
                  programs is now supported.  Use of FAR buffers does
                  not in any way affect the speed of the routines.







         async_peek
         ---------------------------------------------------------------

         Purpose: Indexed receive ring buffer look ahead function.

         Format:  int async_peek(port, index);
                   ASYNC *port;       Pointer to ASYNC structure
                   int index;         Index value

         Examples:

                  ASYNC *port;
                  char ch, buf[10];
                  int i;

                   /* peek next char in receive ring buffer */
                  ch = async_peek(port, 0);

                   /* peek next 10 chars in receive ring buffer */
                  for (i = 0; i < 10; i++)
                      buf[i] = async_peek(port, i);

         Returns: This function returns the character in the receive
                  ring buffer at the indexed position.  If an attempt is
                  made to peek deeper in the ring buffer than there are
                  characters in the ring buffer, -1 (0xffff) is
                  returned.

         Remarks: No characters are removed from the ring buffer by this
                  function.

                  The index value is 0 based.

                  To avoid confusing the character, '\0xff', from the
                  error return value, 0xffff, use an integer size
                  variable for the return value.  The character '\0xff'
                  is returned as 0x00ff and the error condition is
                  returned as 0xffff.







         async_regs
         ---------------------------------------------------------------

         Purpose: Provides direct access to the UART registers.

         Format:  int async_regs(port, reg_ofst, value);
                   ASYNC *port;       Pointer to ASYNC structure
                   int reg_ofst;      Offset of register from base adrs
                   int value;         Value to write or -1 if reading

         Examples:

                  ASYNC *port;
                  int LCRvalue;

                   /* read the line control register */
                  LCRvalue = async_regs(port, LCRreg, RDreg);

                   /* write a 0 to the modem control register */
                  async_regs(port, MCRreg, 0);

         Returns: When reading a register, the return value is the value
                  of the UART register that was read.  When writing a
                  register, the return value is undefined.

         Remarks: The following values for register offsets are defined
                  in COMM.H for use with async_regs:
                    RXreg, TXreg - receive & transmit regs, value = 0
                    IERreg - interrupt enable register,     value = 1
                    IIDreg - interrupt identification reg,  value = 2
                    FCRreg - FIFO control register          value = 2
                    LCRreg - line control register,         value = 3
                    MCRreg - modem control register,        value = 4
                    LSRreg - line status register,          value = 5
                    MSRreg - modem status register,         value = 6
                    LObaud - offset of low baud divisor,    value = 0
                    HIbaud - offset of high baud divisor,   value = 1
                  Also RDreg is defined as -1 for use when reading one
                  of the UART registers.  See the examples.  See
                  cautions on the following page before using this
                  function.







         async_regs
         ---------------------------------------------------------------

         Remarks (continued):

                  This function is provided primarily as a debugging
                  tool.  Reading or writing to the UART registers while
                  operating in an interrupt driven mode can cause
                  several types of problems.  Do not use this function
                  unless you know what you are doing.  Do not read the
                  RXreg, IIDreg, LSRreg, or MSRreg on an open port
                  except for debugging purposes.  Do not write any of
                  the registers.

                  The function may be used on a port that has not yet
                  been opened if the ComBase member of the port struc-
                  ture has been set.  When async_regs is used with an
                  unopened port the UART registers may be read or writ-
                  ten without restriction.







         async_reset
         ---------------------------------------------------------------

         Purpose: Clear parity error bit, framing error bit, character
                  overrun bit, receive buffer overflow bit, and break
                  signal received bit in the the Stat1 byte.

         Format:  void async_reset(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  if (error)
                      async_reset(port);


         Returns: No return value

         Remarks: This function is implemented as a macro.  See also
                  async_rx and async_stat.







         async_restart
         ---------------------------------------------------------------

         Purpose: Re-initialize an already opened serial port

         Format:  void async_restart(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  async_restart(port);


         Returns: No return value

         Remarks: Async_restart resets the interrupt vector, UART regis-
                  ters, and 8259 interrupt controller mask to the values
                  necessary for interrupt driven operation.  It also
                  flushes the receive and transmit buffers and resets
                  the Stat1 byte.  Use this function to restart a comm
                  port after spawning a program that may have altered
                  the interrupt vector, UART regs, or interrupt mask.

                  See also async_stop.







         async_rts
         ---------------------------------------------------------------

         Purpose: Sets or resets the Request to Send signal.

         Format:  void async_rts(port, flag);
                   ASYNC *port;       Pointer to ASYNC structure
                   int flag;          Set/Reset RTS flag

         Example:

                  ASYNC *port;

                  if (WantToDropRTS)
                      async_rts(port, 0);
                  else if (WantRTShigh)
                      async_rts(port, 1);


         Returns: No return value

         Remarks: The RTS signal is primarily used for hardware hand-
                  shaking.  When a port is first opened RTS is set HIGH
                  (enabled).  When the port is closed, it is restored to
                  the condition it was in when the port was opened.  To
                  force RTS low when closing a port, regardless of its
                  state when the port was opened, AND the port member,
                  OldMCR with NOT B_RTS.  To force RTS to remain high
                  when the port is closed, OR OldMCR with B_RTS.

                    Force low:    port->OldMCR &= ~B_RTS;
                                  async_close(port);

                    Force high:   port->OldMCR |= B_RTS;
                                  async_close(port);







         async_rx
         ---------------------------------------------------------------

         Purpose: Gets one character from the receive ring buffer.

         Format:  int async_rx(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Examples:

                  ASYNC *port;
                  int rxch;

                  rxch = async_rx(port);       /* rxch == Stat1/char */

                  rxch = async_rx(port) & 0xff;      /* rxch == char */

                   /* chk if char available & process only if it was */
                  if (!((rxch = async_rx(port)) & B_RXEMPTY)
                      procRxdChar(rxch & 0xff);

         Returns: Async_rx returns the character received as the low
                  byte and the Stat1 status byte as the high byte.  If
                  the receive ring buffer was empty when async_rx was
                  called the low byte will be 0 and the high byte will
                  have the B_RXEMPTY bit set.  The Stat1 byte is a bit
                  mapped value that reflects parity errors, framing
                  errors, character overrun errors, receive buffer
                  overflow errors, receive buffer empty, break signal
                  received, and carrier lost.  If no receive errors
                  have occurred, a break signal has not been received,
                  and a carrier is present, Stat1 will be 0.







         async_rx
         ---------------------------------------------------------------

         Remarks: Error bits set in the Stat1 byte are not necessarily
                  associated with the character just taken out of the
                  receive ring buffer.  In fact, they probably are not.
                  The error bits are set when the error is detected and
                  reset when async_reset is called.  For example:

                   1) 20 bytes of data are received with no errors.
                   2) Async_rx has been called 10 times so 10 characters
                      have been taken out of the ring buffer and 10 of
                      the bytes with no errors are still in the buffer.
                   3) A parity error occurs on the next byte received
                      from the UART -- the 11th byte in the receive ring
                      buffer.
                   4) The next byte taken out of the buffer, which is
                      the first of the 10 remaining good bytes will have
                      the parity error bit in the Stat1 byte.  It will
                      remain set until async_reset is called.

                  If the 'ignore characters with errors' bit is set (see
                  async_ignerr), then characters that have either parity
                  or framing errors are never placed in the receive ring
                  buffer.  They are read from the UART and discarded.
                  The error bits in Stat1 are set regardless of the
                  setting of the 'ignore characters with errors' bit.







         async_rxblk
         ---------------------------------------------------------------

         Purpose: Retrieves a block of characters from the receive ring
                  buffer.

         Format:  int async_rxblk(port, buf, maxchars);
                   ASYNC *port;       Pointer to ASYNC structure
                   char *buf;         Buffer for received data
                   int maxchars;      Maximum number of chars to read

         Example:

                  ASYNC *port;
                  char buf[256];
                  int bytesRead;

                  bytesRead = async_rxblk(port, buf, sizeof(buf));

         Returns: Async_rxblk returns the number of bytes read.  This
                  value will be 'maxchars' if there are that many bytes
                  available in the receive buffer.  If there are not
                  'maxchars' in the receive buffer, the entire contents
                  of the receive buffer will be moved to 'buf' and the
                  return value will be the number of bytes that were in
                  the buffer.

         Remarks: Very fast way to read data.  See also async_rx and
                  async_rxblkch.







         async_rxblkch
         ---------------------------------------------------------------

         Purpose: Retrieve bytes from the receive ring buffer until the
                  specified character is found, 'maxchars' are read, or
                  the receive ring buffer is emptied.

         Format:
           int async_rxblkch(port, buf, maxchars, keychar, includekey);
            ASYNC *port;      Pointer to ASYNC structure
            char *buf;        Destination for bytes read
            int maxchars;     Maximum number of chars to read
            char keychar;     Character to scan for
            int includekey;   Flag set if 'keychar' is to be read also

         Example:

           ASYNC *port;
           char buf[256];
           int bytesRead;
           int foundkey;

           bytesRead = async_rxblkch(port, buf, sizeof(buf), '\n', 1);
           if (bytesRead < 0)
               bytesRead = -bytesRead, foundkey = TRUE;
            else
               foundkey = FALSE;

         Returns: This function returns the number of bytes read if the
                  'keychar' is not found.  If the 'keychar' is found the
                  2's complement of the number of bytes read is
                  returned.







         async_rxblkch
         ---------------------------------------------------------------

         Remarks: The 'includekey' flag, which is the last argument of
                  the function, determines whether or not the 'keychar'
                  is to be included if it is found.  If the flag is 1
                  and the 'keychar' is found it will be the last char-
                  acter in the user buffer.  If this flag is 0 and the
                  'keychar' is found, the 'keychar' is left in the re-
                  ceive ring buffer and will be the first character read
                  when you next call one of the async_rx type functions.
                  This can cause a problem if you set this flag to 0 and
                  the 'keychar' is the first character in the receive
                  buffer.  The function will return 0, which would seem
                  to indicate that there were no bytes in the buffer.
                  Actually the character was found but since you are not
                  taking it out of the ring buffer zero bytes are read.
                  There are two ways to check for this condition.  You
                  can first call async_rxcnt to verify there are bytes
                  in the receive buffer and then call async_rxblkch.  If
                  async_rxblkch returns 0, the 'keychar' is there and is
                  the first byte in the buffer.  The other method is to
                  use async_peek to see what the next character in the
                  receive buffer is before calling async_rxblkch.

                  A 2's complement value of the bytes read is returned
                  by async_rxblkch when the 'keychar' is found.  For
                  actual bytes use:
                      bytes = async_rxblkch( ....);
                      if (bytes < 0)
                          bytes = -bytes;
                  A byte count less than zero is the signal the
                  'keychar' was found.  (Except for the circumstance
                  noted in the previous paragraph).

                  See async_rx, async_rxblk, async_rxcnt, async_peek.







         async_rxcnt
         ---------------------------------------------------------------

         Purpose: Returns the number of bytes in the receive ring
                  buffer.

         Format:  int async_rxcnt(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  BytesInRxBuf = async_rxcnt(port);

         Returns: Number of bytes in the receive ring buffer

         Remarks: This function is implemented as a macro.







         async_rxerr
         ---------------------------------------------------------------

         Purpose: Checks if a receive error has been detected.

         Format:  int async_rxerr(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int rxerr_status;

                  rxerr_status = async_rxerr(port);

         Returns: ZR if no receive errors have been detected, NZ if
                  receive error has been detected.

         Remarks: Types of receive errors that are detected by this
                  function are parity errors, framing errors, UART
                  receive register overflow, and receive ring buffer
                  overflow.  This information is also returned as the
                  high byte of the async_rx and async_stat functions.
                  This function is implemented as a macro.

                  See also async_rx, async_stat.







         async_rxflush
         ---------------------------------------------------------------

         Purpose: Empties out the receive ring buffer.

         Format:  void async_rxflush(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  async_rxflush(port);

         Returns: This function does not have a return value

         Remarks: Clears the receive ring buffer and -- if a 16550 is
                  present in the system with its FIFOs activated --
                  resets the receiver FIFOs.  All data that was in the
                  buffer is lost.  If XON/XOFF flow control is being
                  used and an XOFF has been sent to the remote, this
                  function automatically sends an XON.  An XON is not
                  ALWAYS sent -- only if XFLOW control is in use and the
                  async interrupt routine has sent an XOFF.  It will not
                  clear false XOFFs the remote may have received.







         async_rxfree (5.40)
         ---------------------------------------------------------------

         Purpose: Returns the number of bytes left available in the
                  receive ring buffer for incoming characters.

         Format:  int async_rxfree(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                   RxBufFreeSpace = async_rxfree(port);

         Returns: Number of bytes that can be received without taking
                  any out before a receive buffer overflow will occur.

         Remarks: This function is implemented as a macro.







         async_setbpds
         ---------------------------------------------------------------

         Purpose: Change the baud rate, parity, number of data bits or
                  number of stop bits on an already opened port.

         Format:  int async_setbpds(port, params);
                   ASYNC *port;       Pointer to ASYNC structure
                   char *params;      Pointer to parameter string

         Example:

                  ASYNC *port;
                  int rcode;

                  rcode = async_setbpds(port, "2400E71");

         Returns: This function returns 0 if successful and the new
                  parameter string is copied to the port structure
                  member, BPDSstr.  Errors that can be returned are
                  R_BAUDERR, R_PARITYERR, R_DTABITERR, or R_STPBITERR.
                  If one of these error codes are returned, the port
                  settings are unchanged and the port member BPDSstr is
                  left unchanged.

                  See async_open for a more complete description of
                  these errors.

         Remarks: If 7 data bits is selected the StripMask is set to
                  strip the high bit off incoming data.  If 8 data bits
                  are selected the StripMask is disabled.

                  Valid baud rates are from 50 to 115200 baud.  Parity
                  may be 'E'ven, 'N'one, or 'O'dd.  The number of data
                  bits must be 7 or 8 and the number of stop bits must
                  be 1 or 2.  Do not use spaces, commas, or any other
                  type of punctuation in the parameter string.

                  See also async_open, async_strip.







         async_sndbrk
         ---------------------------------------------------------------

         Purpose: Enable or disable a break signal

         Format:  void async_sndbrk(port, Brkflag);
                   ASYNC *port;       Pointer to ASYNC structure
                   int Brkflag;       Set/Reset break signal flag

         Example:

                  ASYNC *port;

                   /* send break for 50 msec */
                  async_sndbrk(port, 1); /* enable break signal */
                  delay(50MSEC);         /* your delay function */
                  async_sndbrk(port, 0); /* disable break signal */


         Returns: No return value

         Remarks: This function causes the UART to send a continuous
                  break signal if it is called with the flag set to 1.
                  It must be called again with the flag set to 0 to
                  disable the break signal.







         async_stat
         ---------------------------------------------------------------

         Purpose: Get the current status of a port

         Format:  int async_stat(port, mask);
                   ASYNC *port;       Pointer to ASYNC structure
                   int mask;          Mask applied to return value

         Examples:

                  ASYNC *port;
                  int status;

                   /* status = all status bits */
                  status = async_stat(port, 0xffff);

                   /* check for XOFF received condition */
                  if (async_stat(port, B_XRXD))
                      do_something();


         Returns: Returns Stat1/Stat2 status bits after masking them
                  with the passed mask value.  Stat1 is the high byte
                  and Stat2 is the low byte of the return value.

                  Stat1 bit map:
                      Bit 7 = set if no carrier present
                      Bit 6 = receive ring buffer empty
                      Bit 5 = used by interrupt routines (always 0)
                      Bit 4 = break signal was detected
                      Bit 3 = framing error was detected
                      Bit 2 = parity error was detected
                      Bit 1 = character overrun error was detected
                      Bit 0 = receive ring buffer has overflowed

                  Stat2 bit map:
                      Bit 7 = carrier detect monitored for flow control
                      Bit 6 = XOFF rx'd or hardware flow control active
                      Bit 5 = data set ready monitored for flow control
                      Bit 4 = clear to send monitored for flow control
                      Bit 3 = transmit ring buffer is empty
                      Bit 2 = an XOFF has been sent by interrupt handler
                      Bit 1 = an XOFF has been received
                      Bit 0 = using XON/XOFF flow control







         async_stat
         ---------------------------------------------------------------

         Remarks: For some situations, it is more efficient to use one
                  of the other library functions targeted specifically
                  for the information you want.  For instance, instead
                  of calling:
                       async_stat(port, B_XRXD);
                  use:
                       async_xrxd(port);

                  The information in the Stat1 byte is also returned as
                  the high byte of the async_rx function.  Bits 0-4 of
                  Stat1 remain set until cleared by the async_reset
                  function.

                  Not all bits in the Stat2 and Stat1 port structure
                  members are kept updated on a constant basis so do not
                  try to check a condition by testing the Stat1 or Stat2
                  values in the ASYNC structure.  Use one of the docu-
                  mented functions or macros to be sure of getting the
                  correct result.







         async_stop
         ---------------------------------------------------------------

         Purpose: Temporarily disables interrupt driven operation of an
                  already opened port.

         Format:  void async_stop(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int x, inhdl, outhdl, errhdl;

                  async_stop(port);               /* release port */
                   /* redirect console to async port */
                  x = open("COM1", O_RDWR|O_BINARY);
                  inhdl = dup(0);  outhdl = dup(1);  errhdl = dup(2);
                  dup2(x, 0);  dup2(x, 1);  dup2(x, 2);
                   /* run a redirected DOS shell */
                  spawnlp(P_WAIT, "COMMAND.COM", "COMMAND.COM", NULL);
                   /* restore stdin, stdout, stderr */
                  close(x);
                  dup2(inhdl, 0);   close(inhdl);
                  dup2(outhdl, 1);  close(outhdl);
                  dup2(errhdl, 2);  close(errhdl);
                  async_restart(port);   /* regain control of port */

         Returns: No return value

         Remarks: Call this function before spawning a program that will
                  be doing its own port I/O, such as an external commun-
                  ications program or a redirected DOS shell.  After the
                  other application has completed, call async_restart to
                  re-enable interrupt operation.

                  This function disables interrupts for the named port
                  by clearing UART's interrupt enable register and the
                  OUT2 bit of its modem control register.

                  See also async_restart.







         async_strip
         ---------------------------------------------------------------

         Purpose: Set the strip mask for received characters.

         Format:  void async_strip(port, mask);
                   ASYNC *port;       Pointer to ASYNC structure
                   char mask;         Strip mask

         Example:

                  ASYNC *port;

                  async_strip(port, '\x7f');

         Returns: No return value

         Remarks: The strip mask is automatically set to 0x7f when the
                  parameters are set for 7 data bits and to 0xff when 8
                  data bits are used.  All incoming data is ANDed with
                  the strip mask before it is placed in the receive ring
                  buffer.  This function is implemented as a macro.







         async_tx
         ---------------------------------------------------------------

         Purpose: Send 1 character to a port.

         Format:  int async_tx(port, ch);
                   ASYNC *port;       Pointer to ASYNC structure
                   char ch;           Character to transmit

         Example:

                  ASYNC *port;

                   /* send a CR/LF to a port */
                  async_tx(port, '\r');
                  async_tx(port, '\n');


         Returns: Returns the number of bytes left available in the
                  transmit ring buffer unless the ring buffer was full
                  when the function was called.  R_TXERR is returned if
                  the transmit ring buffer was full and the character
                  that was to be transmitted is not placed in the ring
                  buffer.

         Remarks: The error return value, R_TXERR, is a negative number.
                  The bytes free return value can never be negative.

                  See also async_txblk, async_txfree.







         async_txblk
         ---------------------------------------------------------------

         Purpose: Send a block of characters to a port.

         Format:  int async_txblk(port, buf, count);
                   ASYNC *port;       Pointer to ASYNC structure
                   char *buf;         Pointer to block to transmit
                   int count;         Size of block in bytes

         Examples:

                  ASYNC *port;
                  char buf[128];
                  static char *msg = "Send this message\r\n");

                  put_data_in_buf();
                  async_txblk(port, buf, sizeof(buf));
                  async_txblk(port, msg, strlen(msg));

         Returns: Returns the number of bytes left available in the
                  transmit ring buffer unless the ring buffer would not
                  hold the entire block when the function was called.
                  R_TXERR is returned if there was no room for the
                  block and none of the bytes in the block are sent.

         Remarks: This function is much faster than using repeated calls
                  to async_tx when multiple bytes are being transmitted.
                  The error return value, R_TXERR, is a negative number.
                  The bytes free return value can never be negative.

                  See also async_tx, async_txfree.







         async_txcnt (5.40)
         ---------------------------------------------------------------

         Purpose: Returns the number of bytes in the transmit ring
                  buffer.

         Format:  int async_txcnt(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  BytesInTxBuf = async_txcnt(port);

         Returns: Number of untransmitted bytes in the transmit ring
                  buffer.

         Remarks: This function is implemented as a macro.  If a 16550
                  is in the system with its FIFOs active, there may be
                  up to 16 (depends on what async_FIFOtxlvl is set at --
                  the default is 3 bytes) more bytes of untransmitted
                  data in the 16550 FIFOs plus 1 byte in the UART
                  transmit hold register.  With no 16550 there may still
                  be up to 2 untransmitted bytes -- one in the UART's
                  transmit hold register and one in the UART's transmit
                  shift register.  To monitor for a transmit buffer
                  empty condition use async_txempty.







         async_txempty
         ---------------------------------------------------------------

         Purpose: Checks if transmit ring buffer is empty.

         Format:  int async_txempty(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                   /* wait for transmit ring buffer to empty out */
                  while (!async_txempty(port))
                      ;

         Returns: NZ if the transmit ring buffer is empty, ZR if the
                  buffer still has characters to be transmitted.

         Remarks: This function is implemented as a macro.  If a 16550
                  is in the system with its FIFOs active, there may be
                  up to 16 (depends on what async_FIFOtxlvl is set at --
                  the default is 3 bytes) more bytes of untransmitted
                  data in the 16550 FIFOs plus 1 byte in the UART
                  transmit hold register.  With no 16550 there may still
                  be up to 2 untransmitted bytes -- one in the UART's
                  transmit hold register and one in the UART's transmit
                  shift register.







         async_txflush
         ---------------------------------------------------------------

         Purpose: Flushes the transmit ring buffer.

         Format:  void async_txflush(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  async_txflush(port);


         Returns: No return value

         Remarks: Clears the transmit ring buffer and -- if a 16550
                  operating in FIFO mode is in the system -- resets the
                  transmit FIFOs.  All characters in the buffer that
                  have not been transmitted are lost.







         async_txfree
         ---------------------------------------------------------------

         Purpose: Returns the number of bytes left available in the
                  transmit ring buffer.

         Format:  int async_txfree(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int tx_bytes_available;

                  tx_bytes_available = async_txfree(port);


         Returns: Number of bytes of free space left in the transmit
                  buffer.

         Remarks: The number of free bytes left in the transmit ring
                  buffer is also the return value of async_tx and
                  async_txblk.  This function is implemented as a macro.







         async_xany
         ---------------------------------------------------------------

         Purpose: Checks if accepting the first character after an XOFF
                  is received as the XON character.  DOES NOT enable any
                  character XON (use async_xflow).

         Format:  int async_xany(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int rcode;

                  rcode = async_xany(port);

         Returns: Not zero if first character after an XOFF is to be
                  treated as an XON.  Zero if a real XON is required to
                  clear an XOFF.

         Remarks: This function is implemented as a macro.  See also
                  async_xflow.







         async_xflow
         ---------------------------------------------------------------

         Purpose: Enables/disables use of XON/XOFF flow control.

         Format:  void async_xflow(port, flag);
                   ASYNC *port;       Pointer to ASYNC structure
                   int flag;          Enable/Disable & any char XON flag

         Examples:

                  ASYNC *port;

                  async_xflow(port, B_XUSE); /* use flow control */
                  async_xflow(port, 0);      /* disable flow control */

                   /* use XON/XOFF flow control with any char being
                      accepted as an XON */
                  async_xflow(port, B_XUSE | B_XONANY);

                   /* enable XON/XOFF on transmit side only */
                  async_xflow(port, B_XUSET);

                   /* enable XON/XOFF on receive side only */
                  async_xflow(port, B_XUSER);

         Returns: No return value

         Remarks: Passing B_XUSET enables the transmission of XON/XOFF
                  characters when the receive buffer fills to the 'trip'
                  levels discussed in the following paragraph.  Incoming
                  XON/XOFFs are not regarded as flow control characters
                  and are stored in the ring buffer.  Passing B_XUSER,
                  enables recognition of received XON/XOFFs as flow
                  characters but does not enable transmission of
                  XON/XOFF at the trip levels.  If B_XUSE is passed,
                  both transmission and recognition of XON/XOFF as flow
                  characters is enabled (the same as B_XUSET | B_XUSER).
                  ORing B_XONANY with either B_XUSE or B_XUSER causes
                  the first character received after an XOFF to be
                  treated as the XON unless that character is another
                  XOFF.  Passing zero as the flag disables XON/XOFF flow
                  control.  The default is no flow control.







         async_xflow
         ---------------------------------------------------------------

         Remarks (continued):

                  The port structure member, XoffTrip, determines when
                  an XOFF will be sent.  Whenever the number of bytes
                  left available in receive buffer falls below XoffTrip,
                  an XOFF is sent.  The default value of XoffTrip is 25%
                  of the size of the receive buffer so an XOFF is sent
                  whenever the receive buffer is 75% full.

                  The port structure member, XonTrip, determines when an
                  XON will be sent.  Whenever the number of bytes left
                  available in the receive buffer rises above XonTrip,
                  an XON will be sent.  Its default value is 50% of the
                  size of the receive buffer.

                  The port structure member, XTxRptInit, determines how
                  many bytes may be received after an XOFF is sent
                  before another XOFF is sent.  Its default value is
                  6.25% of the size of the receive buffer or 160 bytes,
                  whichever is less.

                  XoffTrip, XonTrip, and XTxRptInit may all be changed
                  from their default values by directly accessing the
                  port structure.  To do this:

                      ASYNC *port;
                     /* send XOFF when 300 bytes left in rx ring buf */
                      port->XoffTrip = 300;
                     /* send XON when 350 bytes left in rx ring buf */
                      port->XonTrip = 350;

                  Be sure to keep the XonTrip level higher than the
                  XoffTrip level.  The values are for bytes left
                  available not bytes used.

                  The XTxRptInit value is used to automatically send
                  another XOFF in the event the first one was ignored.
                  Instead of sending an XOFF character everytime another
                  character is received, the interrupt routines wait for
                  'XTxRptInit' characters to be received and then repeat
                  the XOFF.  If this value is set to low some systems
                  that allow any character to be an XON will treat the
                  repeated XOFF character as an XON.







         async_xoffclr
         ---------------------------------------------------------------

         Purpose: Manually clears an XOFF received condition

         Format:  void async_xoffclr(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  async_xoffclr(port);

         Returns: No return value

         Remarks: Async_xoffclr has the same effect as if the remote
                  system had sent an XON.  This will unstop the system
                  in the event a false XOFF is received or the remote's
                  XON was lost.  Use this function with caution.  Unless
                  something goes wrong, the remote will clear XOFF cond-
                  itions automatically by sending an XON.  If an XOFF is
                  manually cleared, the remote site may be overran and
                  lose data.  For use only when XON/XOFF flow control
                  has been activated.

                  See also async_xoffset.







         async_xoffset
         ---------------------------------------------------------------

         Purpose: Manually sets an XOFF received condition

         Format:  void async_xoffset(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  async_xoffset(port);

         Returns: No return value

         Remarks: Forces the local site to act as though an XOFF had
                  been received.  Transmit interrupts are disabled until
                  the remote sends an XON or you call async_xoffclr.
                  For use only when XON/XOFF flow control has been
                  activated.

                  See also async_xoffclr.







         async_xrxd
         ---------------------------------------------------------------

         Purpose: Check if an XOFF has been received and has activated a
                  flow control halt.

         Format:  int async_xrxd(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int rcode;

                  rcode = async_xrxd(port);

         Returns: Not zero if an XOFF has been received and an XON has
                  not been received to clear it.  Returns zero if XOFF
                  flow halt is not currently active.

         Remarks: This function is implemented as a macro.  See also
                  async_xoffclr, async_xtxd.







         async_xtxd
         ---------------------------------------------------------------

         Purpose: Check if an XOFF has been sent

         Format:  int async_xtxd(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;
                  int rcode;

                  rcode = async_xtxd(port);

         Returns: Not zero if an XOFF has not been sent by the receive
                  interrupt routine and an XON has not been sent to
                  clear it.  Returns zero if an XOFF has not been sent.

         Remarks: This function is implemented as a macro.  See also
                  async_xoffclr, async_xrxd.







         async_xuse
         ---------------------------------------------------------------

         Purpose: Check if XON/XOFF protocol is currently being used

         Format:  int async_xuse(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  rcode = async_xuse(port);

         Returns: Not zero if XON/XOFF protocol is being used on either
                  the transmit or receive sides, zero if XON/XOFF flow
                  is not being used at all.

         Remarks: This function is implemented as a macro.  See
                  async_xflow, async_xuset, async_xuser.







         async_xuser
         ---------------------------------------------------------------

         Purpose: Check if XON/XOFF protocol is enabled on the receive
                  side (receiver recognizes XON/XOFF as flow control).

         Format:  int async_xuser(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  rcode = async_xuser(port);

         Returns: Not zero if XON/XOFF protocol is being used on the
                  receive side, zero if it is not.

         Remarks: This function is implemented as a macro.  See
                  async_xflow, async_xuset, async_xuse.







         async_xuset
         ---------------------------------------------------------------

         Purpose: Check if XON/XOFF protocol is enabled on the transmit
                  side (transmitter sends XOFF/XON as receive buffer
                  bytes available crosses trip levels).

         Format:  int async_xuset(port);
                   ASYNC *port;       Pointer to ASYNC structure

         Example:

                  ASYNC *port;

                  rcode = async_xuset(port);

         Returns: Not zero if XON/XOFF protocol is being used on the
                  transmit side, zero if it is not.

         Remarks: This function is implemented as a macro.  See
                  async_xflow, async_xuser, async_xuse.