Program STSORBIT

                  Space Shuttle and Satellite Orbit Simulation






                  (C) Copyright David H. Ransom, Jr., 1989-1990
                              All rights reserved.







                                  Version  9123
                                  June 02, 1991




                             by David H. Ransom, Jr.
                             Rancho Palos Verdes, CA

                               BBS: (213) 541-7299


   Program STSORBIT Space Shuttle Orbit Simulation                    Page i




                                TABLE OF CONTENTS
                                -----------------

   INTRODUCTION ......................................................1
   PROGRAM DESCRIPTION ...............................................5
   STSORBIT FILES ....................................................7
   STARTING PROGRAM STSORBIT .........................................8
   STSORBIT MAIN MENU ................................................11
     F1  Program STSORBIT Demonstration ..............................11
     F2  Read NASA/NORAD 2-Line Elements .............................12
     F3  Read Prior Mission Information from *.INI File ..............13
     F4  Enter New Orbital Information ...............................14
     F5  Adjust Orbital Parameters ...................................15
         2-Line Elements Model .......................................15
         Simple Orbital Model ........................................16
     F6  Set Elapsed Time Option (2-line elements only)...............17
     F8  Set Program TIME and DATE....................................18
     F9  DOS Shell ...................................................21
     F10 Set STSORBIT Program Options and Features ...................21
     ENTER  Resume Mission ...........................................22
     ESC    Quit STSORBIT and Save Current Mission ...................22
   PROGRAM OPTIONS AND FEATURES MENU .................................23
     F1  Program STSORBIT Information ................................23
     F2  Set New Local Coordinates ...................................23
     F3  Set Display Features ........................................25
     F6  Set Map Center (USA/Europe) .................................25
     F7  Set for SLOW COMPUTER or NO COPROCESSOR .....................26
     F9  Set UTC Time Offset and Daylight Flag .......................26
     F10 Enable/Disable Printer Logging ..............................27
   SET DISPLAY FEATURES ..............................................29
     F2  Display TDRS Coverage .......................................29
     F3  Enable/Disable Additional Map Grid Lines ....................29
     F4  Display NASA Tracking Stations ..............................30
     F5  Show Ascending & Descending Node Data .......................30
     F6  Display Spacecraft Circle of Visibility .....................30
     F7  Display South Atlantic Anomaly Zone .........................30
     F8  Display Terminator, Sun and Spacecraft Lighting .............30
     F9  Select Distance Units: NM or KM .............................31
     F10 Select Satellite Coordinates: RA/DEC, AltAz or XYZ ..........31
   USING GROUND TRACK DISPLAY OPTIONS ................................32
   THE STSORBIT GROUND TRACK DISPLAY .................................34
     On-line Help (F1 Key) ...........................................34
     World Map .......................................................34
     Spacecraft or Satellite and Orbit Projections ...................35
     User's Circle of Visibility .....................................35
     Spacecraft Circle of Visibility .................................36
     TDRS Satellite Features .........................................36
     NASA Ground Tracking Stations ...................................37
   STSORBIT'S ORBITAL MODELS .........................................38
   ADJUSTING ORBITAL PARAMETERS (Simple Orbital Model) ...............40
   STSORBIT REVISION HISTORY .........................................42

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 1


   INTRODUCTION
   ------------

        Program STSORBIT is an orbital tracking and display program for use 
   during Space Shuttle missions, for simulating a Space Shuttle mission, or 
   for general satellite tracking using NASA/NORAD 2-Line Elements. STSORBIT 
   is copyrighted software; you are hereby granted a non-exclusive license for 
   non-commercial or educational use only. Use it if you like it, discard it 
   if you don't. There are no warranties of any kind. If you wish to use 
   STSORBIT commercially, write for license information. The only request I 
   make of users is that they take the time to complete and return the 
   confidential questionnaire in file README. The questionnaire gives users a 
   chance to offer comments and suggestions, and lets me know that people use 
   and appreciate STSORBIT.
        Program STSORBIT is intended to display the orbital position and 
   ground track of the Space Shuttle on a global map during a typical NASA 
   mission. When used with NASA/NORAD 2-Line Elements, the position and ground 
   track of other satellites, such as the Hubble Space Telescope, Gamma Ray 
   Observatory, or the Soviet MIR Space Station, may also be displayed. Data 
   for over 100 different satellites is included. An IBM-compatible computer 
   is required. When used with an EGA or VGA video adapter, the display is in 
   color; CGA and HGC systems can only present graphics in monochrome. In the 
   past, NASA has not published or made available very precise information as 
   to the orbital parameters either before or during a "normal" mission; 
   recently, however, more accurate data has been published in magazines such 
   as Aviation Week and in various NASA publications. NASA now also releases 
   the "2-Line Elements", classical orbital elements which enable much more 
   precise calculation of orbital positions. Military missions, of course, are 
   almost completely blacked out. It is something of a challenge, therefore, 
   to devise a program which will at least come close and which, as more or 
   different information becomes available, will permit the program's data to 
   be updated "on the fly". The primary objective is to present an interesting 
   and attractive real time graphics display of a Space Shuttle mission or 
   satellite ground track, rather than to generate mathematically precise 
   positional information.
        The initial premise of STSORBIT was to attempt to duplicate the wall 
   map in NASA's Mission Control Center in Houston, Texas. Before I started 
   this project, I had seen  several other programs which attempted to do that 
   same task, but each fell short of my objectives for one reason or another; 
   since then other programs have appeared which produce similar information, 
   most notably Paul Traufler's excellent TRAKSAT. It may be, of course, that 
   others will judge this effort lacking as well. One problem is that of size 
   and resolution: the wall map at Mission Control Center is some twenty feet 
   wide with an impressive pixel resolution, very different from the typical 
   personal computer and the size and resolution of its monitor. The NASA wall 
   map shows essentially the entire globe in a cylindrical projection; 
   STSORBIT uses a cylindrical projection but restricts the vertical display 
   to latitudes from +80 degrees to -80 degrees in order to achieve reasonable 
   proportions and vertical resolution while at the same time showing 
   recognizable land features.
        As a consequence of the basic inaccuracies relative to the orbital 
   parameters of a Space Shuttle mission while it is in progress, I did not 
   originally try to be especially precise with respect to the orbital 
   mathematics. Additionally, mathematical complexity must be held to a 
   reasonable minimum if older computers not equipped with a math coprocessor 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 2


   are to be able to maintain the presentation in real time. The higher 
   resolution and color graphics available with more advanced displays such as 
   the EGA and VGA greatly enhance the program, but my Zenith laptop computer 
   emulates the older CGA graphics display in (blue) monochrome. Therefore, in 
   order to use my program on all of my own computers, STSORBIT maintains 
   compatibility with all three display standards. Recently, compatibility 
   with HGC (Hercules Graphics Card) has been improved.
        My somewhat casual attitude toward mathematical precision changed with 
   the launch of the Hubble Space Telescope (HST) and the regular availability 
   of NASA/NORAD 2-Line Elements via modem. Until HST, I had been content to 
   update the orbital data occasionally during the course of a typical five 
   day mission and live with the errors inherent in my original orbital model. 
   The accuracy of that model degrades rapidly after five or ten orbits and, 
   although it may be the only method available at the start of a mission, 
   more accurate data are now readily available within a day or so of launch. 
   The NASA SpaceLink BBS in Huntsville, Alabama also began posting 2-line 
   orbital elements for the Space Shuttle in early 1991 due in part to my 
   continuing suggestions.
        Beginning with Version 9022, therefore, STSORBIT was modified to also 
   read orbital data from these NASA 2-line elements and thereby maintain 
   significantly improved accuracy over longer periods of time. As an 
   incidental benefit, the ground tracks of other satellites (such as the 
   Russian space station MIR) may now also be displayed. At present, the 
   orbital model (SGP4) used with 2-line elements is accurate only for low 
   Earth orbits. Deep space orbits, defined as orbits having an orbital period 
   greater than or equal to 225 minutes, require a more complex orbital model 
   (SDP4) for best accuracy; STSORBIT calculates data and displays a ground 
   track for deep space objects but the accuracy of these data has not been 
   carefully validated; it is believed to be "reasonably" accurate.
        In mid-1990, STSORBIT found its way to the NASA Johnson Space Center 
   in Houston, Texas. Quite a few individuals from JSC sent me comments and 
   suggestions for further improving the program, among them Ron Parise of the 
   STS-35/ASTRO-1 crew. Ron suggested that I make modifications to allow the 
   display of Mission Elapsed Time (MET) for shuttle missions while using the 
   NASA 2-line elements. This would allow both the higher accuracy of the NASA 
   orbital data and permit following the mission timeline using MET. Although 
   the launch time and date must be entered independently of the 2-line 
   elements, the MET capability has now been added. Another suggestion from 
   Ron and others was to include the sun terminator.
        A brief biographical note: I am a retired physicist and engineer who 
   spent all of his professional life in the world of electronics, data 
   communications and, more recently, computers. As a young man I was actively 
   involved in the early American space program, including projects such as 
   Ranger, Mariner, Mercury, and Apollo; my interest in space has continued to 
   this day. The desire to "keep in touch" with our Space Shuttle missions was 
   one of the principal incentives in the development of this software. If 
   STSORBIT also serves to help spark the interest of young people in science 
   and technology or can be a learning tool at any level, I will have more 
   than achieved my goal.
        In addition to individual users all over the world, STSORBIT is also 
   being used in an educational setting. At a middle school in Kansas, the 
   program is projected in the school auditorium from time to time during a 
   mission to show the children graphically what is happening and to give them 
   a sense of "real time" participation in our space program. At an Air Force 
   training facility, STSORBIT is one of many tools used to prepare Air Force 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 3


   officers for their duties in the Air Force Space Command. The program was 
   widely distributed at a recent National Association of Science Teachers 
   convention and by radio amateurs at regional "ham fests".
        For those who are interested in our space program and who have access 
   to a modem, I recommend NASA's SpaceLink Bulletin Board System in 
   Huntsville, Alabama, (205) 895-0028, available twenty four hours per day. 
   NASA SpaceLink, supervised by Bill Anderson of the NASA Marshall Space 
   Flight Center, provides a wealth of information on NASA and its projects. 
   2-line orbital elements for a Space Shuttle mission are usually available 
   while the mission is in progress. In addition to educational materials 
   (including STSORBIT), general information on NASA programs and plans, news 
   releases, and graphics images from prior spacecraft missions such as 
   Voyager, SpaceLink also devotes a complete section to current news and 
   information on the Space Shuttle. I particularly appreciate the STS Mission 
   Press Kit, available about two weeks before each mission, which provides a 
   great deal of information on the upcoming mission, payload and crew as well 
   as broadcast schedules on NASA Select Television, Satellite F2-R, 
   Transponder 13. Mission status reports are generated daily during the 
   course of a mission. I regularly call SpaceLink and post files of interest 
   on my own bulletin board system (BBS).
        Special thanks to Paul Traufler for his friendship and encouragement 
   over the past several years. Our regular telephone conversations have 
   generated many a new idea and the synergism has been beneficial to us both. 
   Our two programs, STSORBIT and TRAKSAT, have engaged us in a friendly 
   rivalry which has, I think, improved both programs many fold. I may have 
   provided the initial spur to Paul to write TRAKSAT (in order to improve on 
   my "sloppy orbital math", as Paul described it) but TRAKSAT has in turn 
   kept my nose to the grindstone. The emphasis of the two programs is 
   slightly different, with STSORBIT concentrating on the graphical display 
   and TRAKSAT on high precision analytical and predictive techniques. I 
   strongly recommend TRAKSAT for the serious satellite tracker. My thanks as 
   well for Paul's help in upgrading STSORBIT to use the NASA/NORAD 2-Line 
   Elements.
        My thanks also to Brian K. Jones and his program SUNMAP (available on 
   my BBS), an interesting program in its own right, for the initial map 
   coordinate data file used in that program. SUNMAP served as a demonstration 
   that a reasonable world map display WAS possible, particularly on EGA and 
   VGA monitors, and encouraged me to start this STSORBIT project.
        Finally, my thanks to all those individuals who have taken the time to 
   write to me or leave a message on my BBS with comments and suggestions. 
   While I haven't been able to implement every suggestion, many are now 
   included and the feedback is most welcome.
        For current orbital information (if a mission is in progress), current 
   NASA/NORAD 2-line element sets and the most recent version of the program, 
   call my bulletin board system (BBS) at (213) 541-7299. If the BBS has not 
   answered after the fourth ring, hang up, wait TWO MINUTES, then call back; 
   the system has a power controller and if the system is off it takes that 
   long for the computer to start up and do its housekeeping chores. The 
   system now has over 850 users and is often busy, so be patient.
        If you do not have access to a modem, you may send US$10.00 to cover 
   materials, postage and handling for a copy of the latest version; please 
   specify 5-1/4" 360K or 3-1/2" 720K disks.

                                           David H. Ransom, Jr.
                                           7130 Avenida Altisima

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 4


                                           Rancho Palos Verdes, CA 90274

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 5


   PROGRAM DESCRIPTION
   -------------------

        A typical Space Shuttle orbit is nearly, but almost never exactly, 
   circular with an altitude of approximately one hundred and sixty nautical 
   miles plus or minus thirty nautical miles and an inclination of from about 
   28 degrees through about 57 degrees. Occasional missions, especially 
   military missions, fly at higher altitudes and/or inclinations and often 
   use more elliptical orbits. Little of this information is known to very 
   good accuracy by the casual listener.
        Initially, therefore, the interested would-be mission observer may 
   have only the time and date of launch to initialize a tracking program. 
   Given the geographical coordinates of the Kennedy Space Center, assuming a 
   circular orbit, and using the typical altitude and inclination of a Space 
   Shuttle orbit, the data should be sufficient to give at least a rough idea 
   of the Shuttle's position for the first several orbits. After that, 
   additional information is required if the position is going to be very 
   close.
        Fortunately, Mission Control Center does occasionally announce the 
   orbital altitude, which is usually in the neighborhood of about one hundred 
   and sixty nautical miles; the reader is cautioned that the popular press 
   and television often (but not always) convert the orbital altitude to 
   statute miles with the inevitable confusion resulting. If a television 
   viewer has access to NASA Select Television on Satcom F2R, Transponder 13, 
   he will periodically see Mission Control Center's huge wall map on which 
   the current position of the Space Shuttle is always displayed. Using this 
   display, the careful viewer can make a visual estimate of the longitude of 
   the ascending or descending node, the point at which the orbit crosses the 
   Earth's equator in the Northbound or Southbound direction respectively. Not 
   exactly high-tech data acquisition, but better than nothing at all!
        Given all of these uncertainties, I did not feel it necessary or 
   worthwhile to try to hone the mathematics of my "simple" orbital model in 
   program STSORBIT beyond that required to give an approximate position in 
   real time. Coincident with the Hubble Space Telescope mission I added the 
   J2 perturbation factor for improved accuracy.
        As an example, STSORBIT was used to track STS-31, Discovery and the 
   Hubble Space Telescope, and gave an accurate position over more than 25 
   orbits. Whenever practical, I generate the information required by STSORBIT 
   as an initialization file, for example HST.INI for the Hubble Space 
   Telescope, which may be read directly by the program and which uses the 
   most current data. These .INI files are normally posted on my BBS during a 
   mission. When orbital parameters change during a mission, as was the case 
   with STS-31, new .INI files are posted as soon as the new data are 
   determined. 
        Within a day or two of launch, the NASA/NORAD 2-line elements are 
   usually available and will yield a more accurate position over longer time 
   periods provided no orbital maneuvers are made. Using NASA/NORAD 2-line 
   elements is quite simple. No adjustment of orbital parameters is necessary 
   when using the 2-line elements. All that is required is to obtain the 
   current 2-line elements file (from my BBS or elsewhere), enter the name of 
   the file (for example, NASA710.TXT) and the name of the desired satellite 
   (HST for Hubble Space Telescope). STSORBIT takes care of all the rest. The 
   2-line element set available at the time of this release of STSORBIT is 
   included in the program files. The data for each satellite included in the 
   2-line element set is referenced to a specific date and time, the "Epoch" 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 6


   of the data. As a general rule, orbital calculations will be relatively 
   accurate for 10 to 20 days after the Epoch date; the lower the orbit, the 
   greater the effect of factors such as atmospheric drag and the less 
   accurate the calculations will be as time passes. Users who prepare their 
   own 2-line element files are cautioned to make certain no extraneous lines 
   are included, that the satellite name is on a single line, and that the two 
   data lines exactly conform to the 69-character/line format.
        Particularly with the relatively low resolution (640x200) of a CGA 
   monitor, the display errors alone are significant; using an EGA or VGA 
   monitor improves the vertical resolution by about a factor of two (640x350 
   or 640x480, respectively), but does nothing to improve the horizontal 
   resolution. The HGC (Hercules Graphics Card) has also been included; HGC 
   users will note that of the 720 horizontal pixels available, only the left 
   640 pixels are used in the present code. Higher resolution monitors are 
   available (at a price!) but are not in general use and so are not suitable 
   for a program such as STSORBIT which is intended for public distribution. 
        STSORBIT displays a portion of the Earth using a cylindrical 
   projection of the surface area almost from one pole to the other; a small 
   area near each pole (approximately ten degrees) is omitted to maintain 
   optimum map proportions. The map shows most of the Earth's land boundaries, 
   and continental areas and major oceans are easily recognizable. At any 
   time, the display shows the Space Shuttle or satellite as a small symbol, 
   the projected orbit for approximately the next three orbits (or four and a 
   half hours), and the orbit track for the past orbit (or one and a half 
   hours).
         The program may be operated in real time or in "fast time", which is 
   ten or sixty times normal time. For "simple" orbits, the orbital parameters 
   may be manually entered or adjusted for the desired mission. A pre-
   programmed demonstration may be run to permit the user to become familiar 
   with the program and its display. The lower section of the screen displays 
   current data about the mission in progress.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 7


   STSORBIT FILES
   --------------

        STSORBIT is normally distributed in archived format using either the 
   PAK or ZIP format. The following files are usually included:

             STSORBIT.EXE        Main program        (required)
             STSORBIT.DOC        Documentation       (not required)
             STSORBIT.MPT        World map data      (required)
             STSORBIT.CTY        City coordinates    (optional)
             STSORBIT.INI        Initialization data (optional)

             MSHERC.COM          Hercules driver     (required for HGC)

             NASAnnn.TXT         2-Line Elements     (optional)
             HST.TXT             HST 2-Line Elements (optional)

             README              STSORBIT Confidential Questionnaire

             QUICK!.DOC          Quick Start Instructions

   Files noted as "(required)" must be in the current default directory for 
   program operation. Files noted as "(optional)" do not need to be in the 
   default directory when STSORBIT is operated but provide additional features 
   or information if present. If file STSORBIT.INI is not present it will be 
   created.

        Program MSHERC must be executed before running STSORBIT for systems 
   equipped with Hercules Graphics Cards (HGC) or Hercules Graphics Plus 
   Cards. STSORBIT will otherwise report an error and remind the user to run 
   MSHERC.

        File NASAnnn.TXT (where "nnn" will be a number such as "847") is a set 
   of NASA/NORAD 2-line elements as of the program release date. Note that the 
   2-line elements should only be used for ten to twenty days after the epoch 
   date for each satellite if reasonable accuracy is to be maintained. Current 
   orbital elements are always available on my bulletin board system.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 8


   STARTING PROGRAM STSORBIT
   -------------------------

        Before starting program STSORBIT, delete the file STSORBIT.INI if it 
   has been created by a previous version of STSORBIT. The format of the .INI 
   file has changed with Version 9046 and, although the program will read 
   prior versions of .INI files, it is safer to "start from scratch".
        To start program STSORBIT, enter one of the following commands:

             STSORBIT            (any monitor, CGA/HGC/EGA/VGA)

             STSORBIT /EGA       (force EGA or lower monitor)

             STSORBIT /CGA       (force CGA monitor)

             STSORBIT /M         (force monochrome operation, EGA/VGA)

             STSORBIT /EUR       (center map on Prime Meridian, EUROPE)

             STSORBIT /R         (resume last mission automatically)

             STSORBIT /S         (force shuttle icon for speed)

        Only one display option (/EGA or /CGA or /M) may be used. Options may 
   be combined and entered in any order. For example, using the following 
   command will resume the prior mission, force the shuttle icon, and force 
   EGA mode:

             STSORBIT /R/S/EGA


                                    * * * * *

                       Hercules Graphics Card USERS NOTE:
                       ----------------------------------
                              
        Run the program MSHERC prior to running STSORBIT. This Microsoft 
   program works with QuickBASIC 4.5 to enable use of the Hercules Graphics 
   Card. One user reported that setting the HGC to FULL and selecting Page 
   Zero (using software supplied with the HGC) was sufficient for proper 
   operation with program STSORBIT. At least one HGC "clone" user reported 
   improper operation.

                                    * * * * *


        If you have already run STSORBIT (or if you have file STSORBIT.INI) 
   and simply wish to resume viewing that same mission, use the /R command 
   line option. STSORBIT will sense the monitor type, enable color for EGA and 
   VGA systems, read the map data as usual, then proceed directly to plotting 
   the mission. The data from the last run, as saved in file STSORBIT.INI, is 
   used to initialize the program. Once started in this manner, pressing the 
   ENTER (or RETURN) key after plotting has started will return to the Main 
   Menu.
        European users, or those users accustomed to viewing a map of the 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 9


   world centered on the Prime Meridian (zero degrees longitude at Greenwich, 
   England), may include the /EUR option by itself or in addition to other 
   options.
        The program automatically checks for the presence of a VGA or EGA and 
   will execute in color if one is found UNLESS the /M command line option is 
   used to force monochrome operation. However, if you wish to operate 
   STSORBIT in the EGA mode when you have a VGA monitor, use the /EGA option. 
   In cases where a monochrome monitor is connected to an adapter which 
   simulates color with gray scale, the /M command line option may be omitted 
   but the various portions of the display may or may not be visible. STSORBIT 
   depends upon Microsoft QuickBASIC to determine whether or not a particular 
   monitor type is available. Some video adapter boards which claim to be VGA 
   are not recognized as such by QuickBASIC and therefore cannot be used in 
   the higher resolution VGA display mode. Similarly, "clone" Hercules 
   Graphics Cards do not always perform correctly.
        The /M option is not required for HGC and CGA graphics operation, 
   since those adapters always render their high resolution graphics in 
   monochrome. Naturally, the operation of the program is enhanced by the use 
   of a color monitor. The vertical resolution is also adjusted depending upon 
   the type of adapter which has been detected. Once STSORBIT has started, the 
   display type may not be changed without halting the program at the Main 
   Menu with the ESC key, then restarting the program with the new option 
   selection(s).
        The program checks for the presence of a math coprocessor and will use 
   it if found. Since the calculations required to determine orbital data are 
   very complex, the use of a math coprocessor will improve the speed of 
   operation by a very substantial amount. Use the SLOW option on the Set 
   Program Options Menu (F10+F7) if the program has difficulty operating on 
   your system.
        STSORBIT normally selects the icon or symbol used to graphically 
   represent the satellite based upon the mission name. Names which start with 
   the letters "STS" will use the space shuttle icon and all other missions 
   will use an icon resembling the Hubble Space Telescope. However, the "other 
   satellite" symbol has approximately three times as many pixels (dots) as 
   does the space shuttle symbol and therefore takes longer to draw and erase. 
   If you are using a slower computer or one not equipped with a math 
   coprocessor, using the "/S" option may improve performance by forcing the 
   use of the space shuttle symbol. The /S option may be used by itself or in 
   combination with other options.
        STSORBIT first reads in the map coordinates from file STSORBIT.MPT, 
   which must be in the current drive and directory. These coordinates are 
   converted to screen coordinates for the type of monitor detected and stored 
   internally so that they need only be read once. After map coordinates have 
   been loaded, the initial title screen is shown on the display.
        The title screen is displayed for 15 seconds for normal program 
   operation or for 3 seconds if the /R command line option has been used. The 
   Main Menu, described in the following section is then displayed. Press any 
   key to proceed to the Main Menu immediately.


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 10



                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122



                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    05/21/1991     05/21/1991


                        Last Mission = STS-40 (est) [STS40D01]






                     (C) Copyright David H. Ransom, Jr., 1989-1991
                                 All rights reserved.


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 11


   STSORBIT MAIN MENU
   ------------------

        Once the map coordinates have been stored internally, STSORBIT 
   presents its Main Menu:



                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:34:56 PDT   23:34:56 UTC
                      Current date:    05/21/1991     05/21/1991

            F1     Program STSORBIT Demonstration
            F2     Read NASA/NORAD 2-Line Elements       (from *.TXT File)
            F3     Read Prior Mission Information        (from *.INI File)
            F4     Enter New Orbital Information    (Simple Orbital Model)
            F5     Adjust Launch Time and/or Launch Date
            F6     Display MET & Launch Times     (now 2-Line Epoch Times)
            F8     Set program TIME and/or DATE
            F9     DOS Shell             (CAUTION: DOS Version 3.x+ ONLY!)
            F10    Set STSORBIT Program Options and Features
            ENTER  Resume Mission                (STS-40 (est) [STS40D01])

            ESC    Quit STSORBIT and Save Current Mission

            Select desired function:


   F1     Program STSORBIT Demonstration
   -------------------------------------

        The F1 command may be used to demonstrate the operation of STSORBIT 
   and to verify that the program will operate correctly. No other information 
   is required. The demonstration automatically sets up the data to simulate a 
   mission and clears the screen. A slight delay may follow while the program 
   calculates the initial parameters of the orbit. Then the world map is 
   drawn, the ground track for the first three orbits (approximately) is drawn 
   as a series of dots (green for color monitors), and mission data is 
   displayed at the bottom. Mission Elapsed Time (MET) is set to shortly 
   before launch time and counts down to zero.
        When MET reaches zero, the shuttle symbol appears over Cape Canaveral. 
   For CGA and HGC systems, the shuttle will blink; for EGA and VGA systems, 
   the shuttle will be steady. At first the shuttle will move along the ground 
   track very slowly, simulating the ascent phase of the mission. After 
   several minutes the shuttle reaches orbital altitude and proceeds along the 
   ground track normally, passing a dot every minute. Press F (for Fast time) 
   once or twice to speed up the progress of the simulation. Press ENTER to 
   return to the Main Menu.
        Data are displayed by STSORBIT in standard formats:

            4/05/1990       Date in month/day/year

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 12


             14:33:00       Time in hours:minutes:seconds
           3/09:23:15       MET in days/hours:minutes:seconds
               -69.34       Longitude and Latitude in degrees
                            WEST longitude and SOUTH latitude are negative
               320.50 nm    Altitude in nautical miles

   F2     Read NASA/NORAD 2-Line Elements from *.TXT File
   ------------------------------------------------------

        In order to read the NASA/NORAD 2-line elements, you must have a file 
   with that data. Typical files from my BBS system have names such as 
   "NASA769.TXT" where the "769" corresponds to the particular NASA data set 
   and may change several times per week. A sample file is included with the 
   normal distribution of STSORBIT.
        Entering the F2 command will display the following prompts:

             Read NASA/NORAD 2-Line Element File

             Press ENTER to enter the current default
             name as shown in square brackets [...].


             Enter 2-Line Filename  [NASA769.TXT]:

             Enter desired Satellite Name   [HST]:

        In each case, pressing ENTER will select the default choice shown 
   inside the square brackets. For the example shown, the defaults are the 
   file NASA710.TXT and the satellite HST. If you wish to change the 
   information (or if no default is shown), enter the required information 
   followed by ENTER. For the filename, if no filetype is included, STSORBIT 
   will automatically add ".TXT". For the satellite, only sufficient letters 
   to unambiguously identify the desired satellite, upper or lower case, are 
   required. For example, "Alou" would select "Alouette 1". Once this 
   information has been entered, STSORBIT will attempt to locate the specified 
   file and the data for the requested satellite. Once a satellite matching 
   the requested name is found, the data is displayed:

             Satellite Name:              HST
             Elements File:               NASA769.TXT
             Elements Record #:           91

             Elements Epoch:              90312.61189795
                                          8 NOV 1990 @ 14:41:08 UTC
             Orbit # at Epoch:            2946
             Satellite Number:            20580
             Launch Year:                 1990
             Launch Number:               37
             Launch Piece:                B
             Element Number:              327
             Inclination:                 28.4715
             RA of Ascend Node:           50.186
             Eccentricity:                .0006172
             Arg of Perigee:              184.0423
             Mean Anomaly:                176.0412

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 13


             Mean Motion:                 14.85441208

             Press ENTER to ACCEPT this satellite, OR
             Press any other key to REJECT and continue searching:

        If this is the satellite you wish, press ENTER and the data will be 
   entered into STSORBIT. If, on the other hand, a different satellite is 
   desired, press any other key (such as the SPACE BAR) and STSORBIT will 
   search for another name matching the requested satellite. For example, 
   there are a number of NAVSTAR Global Positioning Satellites usually 
   included in the file with official names such as "GPS-0001", "GPS-0002", 
   "GPS BII-01" and so forth; requesting "GPS" will allow you to cycle through 
   all the available choices. The file NASAnnn.TXT is an ASCII file; it may be 
   helpful to print the file to show the available satellite names. 
        Once the satellite has been selected, STSORBIT will require a brief 
   time to calculate certain required orbital parameters, then will proceed 
   directly to the display of the ground track.
        As a point of interest, the NASA 2-line elements for the Hubble Space 
   Telescope used in the example here are as follows:

        HST        
        1 20580U 90 37  B 90312.61189795  .00004882  00000-0  53771-3 0  3278
        2 20580  28.4715  50.1860 0006172 184.0423 176.0412 14.85441208 29461


   F3     Read Prior Mission Information from *.INI File
   -----------------------------------------------------

        The F3 command displays all files in the current directory with a 
   filetype of .INI and then prompts the user to enter the name of the desired 
   data file. File STSORBIT.INI is the file which has the data from the last 
   time the program was run; to use file STSORBIT.INI, press ENTER. STSORBIT 
   will automatically supply the filetype .INI if you do not include a 
   filetype. If the requested file is not present, an error will be reported. 
   To create new .INI files, enter the desired data then exit STSORBIT and use 
   the DOS COPY command to copy STSORBIT.INI into a file with a the desired 
   name.
        Additional .INI files may be included with the distribution files for 
   satellites of interest at the time of release. These files will have names 
   such as STS28.INI and STS30.INI. Since Space Shuttle missions normally last 
   only five to ten days, using these files at later dates will generate 
   "unusual" mission elapsed times and orbit numbers! Note that the launch 
   time in these files use Coordinated Universal Time (UTC); prior releases 
   (Version 9019 and earlier) of these files included the launch time in 
   PACIFIC standard or daylight time and had to be converted to your local 
   time.
        STSORBIT also expects your computer clock to be set to the correct 
   local time and date; use the DOS TIME and DATE commands. See the F10+F10 
   command below for information on setting the UTC Zone Offset. Of course, 
   you may "fool" STSORBIT by setting your computer time and date to a desired 
   time and date using the DOS TIME and DATE commands, but be aware that for 
   most computers using MS-DOS/PC-DOS 3.3 or greater the hardware clock is 
   also set with these commands. Instead of setting your computer clock to 
   some fictitious time, use STSORBIT's internal time setting functions (F7 on 
   the Main Menu) to set a desired simulation time. This method does not 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 14


   affect your computer's internal hardware or software clocks.


   F4     Enter New Orbital Information (Simple Orbital Model)
   -----------------------------------------------------------

        The F4 command uses the "simple" orbital model and allows the user to 
   enter the orbital altitude, inclination, launch time, and launch date 
   using your local time or UTC (Coordinated Universal Time) or GMT (Greenwich 
   Mean Time, essentially identical to UTC for the purposes of this program) 
   to determine the orbital parameters. If you enter the time and date using 
   local time, it will internally be converted to UTC so that the .INI file 
   will be valid in any time zone. To manually enter orbital data, you will be 
   prompted for the required information. 


                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:34:56 PDT   23:34:56 UTC
                      Current date:    05/21/1991     05/21/1991


                 Enter mission title:             STS Mission Simulation
                 Enter orbit altitude (nm):       160.00 nm  (  296.52 km)
                 Enter orbit inclination (deg):    28.450 degrees
                 Enter Launch Time (HH:MM:SS):     15:58:12 PST  23:58:12 UTC
                 Enter Launch Date (MM/DD/YYYY):     11/13/1990    11/13/1990




                       Press ENTER to accept, SPACE BAR to repeat: _


   The sample above illustrates the data required to generate the simple 
   orbital model. A brief discussion follows for each item.

        Enter mission title:

   Enter the title of the mission, such as "STS-30 ATLANTIS" without the 
   quotation marks. If you press ENTER, the title "STS Mission Simulation" 
   will be used.

        Enter orbit altitude (nm):
           [Add 'km' for altitude in kilometers.]

   Enter the orbit altitude (or average orbit altitude for non-circular 
   orbits), in nautical miles. If you wish to use kilometers, add the letters 
   "KM" (upper or lower case) at the end of the number.

        Enter orbit inclination:


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 15


   Enter the inclination of the orbit in degrees; a decimal fraction is 
   allowed. For example, STS-30 was flown at an inclination of 28.85 degrees 
   and STS-28 used an inclination of 57 degrees. Press ENTER to use the 
   default value of 28.45 degrees.

        Enter Launch Time (HH:MM:SS):
           [Press ENTER for ASAP; add 'U'or 'G' for UTC/GMT]

   Enter the time in the format shown using 24-hour notation and local time. 
   Add the letter "U" to signify UTC (Coordinated Universal Time) or the 
   letter "G" to signify GMT (Greenwich Mean Time, essentially identical to 
   UTC for the purposes of this program). If you enter "U" or "G", the 
   abbreviation used in the menus will be set to "UTC" or "GMT" respectively.
   One or two digit numbers may be used as required. [The comma is also 
   acceptable as a separator in place of the colon.] You may omit seconds [or 
   minutes and seconds] if desired. For example, an entry of "16" will be 
   entered as 16:00:00 or 4:00 PM. Press ENTER for "launch" ASAP, as soon as 
   possible; depending upon the system, this will be in from 30 to 60 seconds 
   from the current time.

        Enter Launch Date (MM/DD/YYYY):
           [or press ENTER for TODAY]

   Enter the date in the format shown. Note that if you requested UTC or GMT 
   when entering the time, the date is interpreted as the UTC/GMT date. The 
   full four digit year is required and be sure to use the SLASH "/" rather 
   than the MINUS "-" as the separator; STSORBIT's internal date algorithms 
   will interpret the minus sign as just that and some rather strange dates 
   can result! You may also use relative dates: -1 will use the prior day, +2 
   will use two days hence, and so forth. Press ENTER to use today's date.

        Press ENTER to accept, SPACE BAR to repeat:

   When all data have been entered, the program pauses for your approval. If 
   all data are correct, press ENTER. Press the SPACE BAR to start over.


   F5     Adjust Orbital Parameters
   --------------------------------

   ADD/CHANGE LAUNCH DATE AND TIME (2-line elements)

        The full F5 command assumes the "simple" orbital model and is 
   abbreviated when using NASA 2-line elements; only the LAUNCH DATE and 
   LAUNCH TIME may be set when using NASA 2-line elements; all other orbital 
   parameters are included in the 2-line elements and may not be altered 
   within STSORBIT. A 2-line element set must have been previously loaded 
   using the F2 command on the Main Menu before the launch date and time may 
   be set or changed.
        Since NASA 2-line elements are usually available within about 24 hours 
   after a space shuttle launch and are far more accurate than the manually 
   entered "simple orbital data", those data should be used when available. 
   However, since most events occuring during a space shuttle mission follow 
   the MET (Mission Elapsed Time) timeline, the time elapsed since launch, it 
   is convenient to show MET. This requires that you obtain the launch date 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 16


   and launch time independent of the 2-line elements and manually enter that 
   data into STSORBIT.

        Enter Launch Time (HH:MM:SS):
           [Press ENTER for ASAP; add 'U'or 'G' for UTC/GMT]

   Enter the time in the format shown using 24-hour notation and local time. 
   Add the letter "U" to signify UTC (Coordinated Universal Time) or the 
   letter "G" to signify GMT (Greenwich Mean Time, essentially identical to 
   UTC for the purposes of this program). If you enter "U" or "G", the 
   abbreviation used in the menus will be set to "UTC" or "GMT" respectively.
   One or two digit numbers may be used as required. [The comma is also 
   acceptable as a separator in place of the colon.] You may omit seconds [or 
   minutes and seconds] if desired. For example, an entry of "16" will be 
   entered as 16:00:00 or 4:00 PM. Press ENTER for "launch" ASAP, as soon as 
   possible; depending upon the system, this will be in from 30 to 60 seconds 
   from the current time.

        Enter Launch Date (MM/DD/YYYY):
           [or press ENTER for TODAY]

   Enter the date in the format shown. Note that if you requested UTC or GMT 
   when entering the time, the date is interpreted as the UTC/GMT date. The 
   full four digit year is required and be sure to use the SLASH "/" rather 
   than the MINUS "-" as the separator; STSORBIT's internal date algorithms 
   will interpret the minus sign as just that and some rather strange dates 
   can result! You may also use relative dates: -1 will use the prior day, +2 
   will use two days hence, and so forth. Press ENTER to use today's date.

        Press ENTER to accept, SPACE BAR to repeat:

   When all data have been entered, the program pauses for your approval. If 
   all data are correct, press ENTER. Press the SPACE BAR to start over.
        Once the launch date and time have been set, this information is 
   saved in file STSORBIT.INI. However, use caution when changing from one 
   satellite to another since this information is NOT cleared automatically.


   ADJUST ORBITAL PARAMETERS (Simple Orbital Model)

        When the orbital parameters change in mid-mission for the "simple" 
   orbital model, use this command to adjust the orbital period/altitude, 
   orbital longitude, and time along orbital track. This technique allows the 
   "launch time" to remain correct, which in turn assures that Mission Elapsed 
   Time is correct, while adjusting the orbital parameters so that the 
   position is displayed correctly in later orbits. The following items may be 
   adjusted; in each case, the required units or input format is shown in 
   parentheses (...) and the current value of the item is shown within square 
   brackets [...]. Press ENTER to leave an item unchanged.


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 17


                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:34:56 PDT   23:34:56 UTC
                      Current date:    05/21/1991     05/21/1991



   Enter MISSION TITLE [STS Mission Simulation]:    STS Mission Simulation
   Enter LAUNCH TIME (HH:MM:SS)    [23:58:12 UTC]:  15:58:12 PST   23:58:12 UTC
   Enter LAUNCH DATE (MM/DD/YYYY)    [11/13/1990]:    11/13/1990     11/13/1990
   Enter ORBIT INCLINATION (degrees) [28.4500x]:    28.4500x
   Enter ORBITAL ALTITUDE (nm)        [ 160.00]:   160.00 nm  (  296.52 km)
   Enter LONGITUDE adjust (deg)     [   0.000x]:     0.000x
   Enter TIME adjust (min)            [  0.000]:     0.000

                       Press ENTER to accept, SPACE BAR to repeat:


        In order to make these adjustments, the current orbital altitude is 
   required, along with the longitude and time of one or more equator 
   crossings (obtained from the NASA Television wall map). NASA is not too 
   good about making sure that the map is on the screen when the Shuttle makes 
   an equator crossing (Northbound is Ascending Node, Southbound is Descending 
   Node); they have a distressing tendency to cut away just before the 
   crossing. With sufficient patience, however, the data can be interpolated 
   from the television screen. In the case of STS-30, the orbital time at 
   Orbit 34 changed to 90.85 minutes and the longitude of the descending node 
   was approximately -36 degrees, crossing at 2/2:18:00 MET. See the section 
   ADJUSTING ORBITAL PARAMETERS below for more information.


   F6     Set Elapsed Time Option
   ------------------------------

        When using NASA 2-line elements, STSORBIT normally displays the time 
   elapsed since the epoch date of the elements in the upper right portion of 
   the data block. This is marked on the display as "T+Epoch". While this 
   information is not of particular value for satellite viewing purposes, it 
   does indicate the relative age of the orbital data. As a general rule, 
   especially for lower Earth orbits, the effects of orbit decay make position 
   predictions less accurate as time passes. Data which are more than 10 or 20 
   days old may produce less accurate positions.
        For a space shuttle mission, however, all mission events are scheduled 
   against the mission timeline and are reckoned in Mission Elapsed Time 
   (MET), the time elapsed since launch. It is therefore useful to be able to 
   display MET during the course of a mission or to review the flight post-
   mission. Unfortunately, the standard NASA/NORAD 2-line element format does 
   not include the launch time and launch date and therefore this information 
   must be secured independently and manually entered into STSORBIT. Once 
   entered, STSORBIT saves the information in file STSORBIT.INI.
        The F6 command may be used to switch the display between Time Since 
   Epoch ("T+Epoch") and Mission Elapsed Time ("MET"). The command description 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 18


   on the Main Menu indicates which mode will be selected if Function Key F6 
   is pressed:

            F6     Display MET & Launch Times     (now 2-Line Epoch Times)

            F6     Display 2-Line Epoch Times     (now MET & Launch Times)

   The first example (the default) indicates that MET will be displayed if the 
   function key is pressed; the second example indicates that the display will 
   return to Time Since Epoch if the function key is pressed. The elapsed time 
   option may also be switched at any time during the tracking display by 
   pressing the "T" key.
        The F6 command checks that you have already entered the launch time 
   and launch date or that it has been read from a previous STSORBIT session 
   from file STSORBIT.INI. However, since the launch time and date are not 
   included in the 2-line orbital elements, no validity check can be made; if 
   you change satellites, be sure to either clear or change the launch time 
   and date. If no launch time and date are present, you will be prompted for 
   the information as if you had pressed function key F5 (see above). The F6 
   command is inactive unless you have read in 2-line elements using function 
   key F2.


   F8     Set Program TIME and DATE
   --------------------------------

        It is often convenient to set the TIME and DATE within STSORBIT to 
   something other than the current system time and date, or to return to the 
   current system time and date if the program time and date have been 
   changed. Press F4 to go to the TIME and DATE Menu:


                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:34:56 PDT   23:34:56 UTC
                      Current date:    05/21/1991     05/21/1991

                       ACTUAL SYSTEM DATE AND TIME SHOWN ABOVE


            F1     Restore SYSTEM date and time (use "real time")
            F2     Set DOS SYSTEM CLOCK using calendar date and time
            F3     Set SIMULATED date and time using calendar date and time
            F4     Set SIMULATED date and time using Mission Elapsed Time

            ENTER  Return to MAIN MENU

            Select desired function:

        The Date and Time Menu, shown above, displays the available time 
   setting functions along with the actual system date and time as determined 
   by the DOS software clock in your computer (even if simulated time is in 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 19


   effect). Both your local date and time, "PST" or Pacific Standard Time in 
   the example, and "UTC" (Coordinated Universal Time) date and time are 
   displayed. If times have been set using the letter "G", the abbreviation at 
   the right will be "GMT" (Greenwich Mean Time).
        If you wish to execute STSORBIT in "real time", cancelling any 
   simulated time that may be in effect, use the F1 command. This will restore 
   the time and date used for the tracking display to that shown at the top of 
   the menu.
        If the actual system date or time displayed is incorrect, use the F2 
   command to correctly set your system clock. If the zone abbreviation or UTC 
   date or UTC time is incorrect, use the Set Program Options command from the 
   Main Menu (F10+F9) to correctly set the UTC Offset and the Daylight Flag.
        Some organizations, NASA for example, continue to use the wording 
   "Greenwich Mean Time" or "GMT" for what is now usually referred to as 
   "Universal Time" or "UT" (and sometimes, depending upon the application, as 
   "UT1" or "UT2"). STSORBIT uses Coordinated Universal Time or "UTC", the 
   time used for civil timekeeping and broadcast by radio stations such as WWV 
   and the BBC. Although technically these different time standards are not 
   exactly the same, the difference is only a maximum of 0.9 seconds and the 
   program treats them all as identical. STSORBIT defaults to the abbreviation 
   "UTC" but if you prefer to use "GMT", enter any simulated time using F3 and 
   include the letter "G" (upper or lower case) at the end. The time 
   abbreviation at the top of the screen will change from "UTC" to "GMT" and 
   will continue using that abbreviation until a time is entered suffixed with 
   "U". 
        Times are always entered as "HH:MM:SS" where HH is HOURS, MM is 
   MINUTES, and SS is SECONDS. The time entry format is very flexible. Leading 
   zeroes are not required. The comma (",") may be used in place of the colon 
   (":") as a separator if desired. SECONDS or MINUTES and SECONDS may be 
   omitted if desired. Time entries are assumed to be local time; to enter UTC 
   or GMT times, add the letter "U" or "G" (upper or lower case) respectively 
   following the entry. For example, the following are valid time entries:

             Entry          Interpreted as
             ------         --------------
             12             12:00:00
             13,1           13:01:00
             4:1:15         04:01:15
             1,1,1          01:01:01
             13,45U         13:45:00 UTC 
             1:20g          01:20:00 GMT

        Dates are always entered as "DD/MM/YYYY" where DD is DAYS, MM is 
   MONTHS, and YYYY is the full four-digit year. The full date must always be 
   entered; leading zeroes are not required. The date entered is assumed to be 
   for the same time zone as the time entered. If local time is entered, the 
   date will be treated as the local date; if UTC (or GMT) time is entered, 
   the date will be treated as the UTC/GMT date.
        After a time or date entry has been read (after you press the ENTER 
   key), STSORBIT reformats the entry to its standard format, clears the 
   characters you entered, and replaces them by the standard format. This 
   provides a double check that the program has interpreted your entry as you 
   wished.
        Press F1 to restore the program date and time to the system date and 
   time. This command reads the DOS clock and restores the program to "real 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 20


   time" operation. If the program date and time have not been changed with 
   the F3 or F4 commands, this command will have no effect.
        Press F2 to set the DOS system clock. Use this command if you wish to 
   change the actual date and time on your system. Note that on many systems 
   using DOS 3.3 or higher, this command will set BOTH the software clock AND 
   the hardware clock.

                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:34:56 PDT   23:34:56 UTC
                      Current date:    05/21/1991     05/21/1991

           CAUTION: This function will change the computer's SYSTEM CLOCK!

                        Press ENTER to leave an item unchanged

                 Enter TIME (HH:MM:SS):                12:37:38 PST
                 Enter DATE (MM/DD/YYYY):                11-11-1990

            Press ENTER to accept, SPACE BAR to repeat: _

   The sample above shows the screen after the time and date entries have been 
   completed. The current ACTUAL system date and time are displayed for 
   approval. Press ENTER to accept the time and date displayed, or press the 
   SPACE BAR to repeat the entries.
        Press F3 to set a simulated date and time. The date and time may be 
   either in the past or in the future. This command does NOT affect the DOS 
   clock in your system! Use the F2 command above to restore the date and time 
   to "real time".

                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                     Simulated time:  13:00:08 PST   21:00:08 UTC
                     Simulated date:    11/08/1990     11/08/1990



                        Press ENTER to leave an item unchanged

            Enter SIMULATED TIME  [12:05:06]:     13:00:00 PST   21:00:00 UTC
            Enter SIMULATED DATE  [11/11/1990]:     11/09/1990     11/09/1990

            Press ENTER to accept, SPACE BAR to repeat: _

   The sample above shows the screen after the time and date entries have been 
   completed. The new SIMULATED date and time are displayed (and counting) for 
   approval. Press ENTER to accept the time and date displayed, or press the 
   SPACE BAR to repeat the entries.
        Press F4 to set a simulated date and time using MET (Mission Elapsed 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 21


   Time). Note that this command will appear ONLY if the mission name begins 
   with the letters "STS", signifying a Space Transportation System (Space 
   Shuttle) mission.

                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9118

                     Simulated time:  00:17:18 PST   08:17:18 UTC
                     Simulated date:    10/09/1990     10/09/1990



                       Enter desired Mission Elapsed Time (MET)

                       Enter MET DAY (NN):             3 day(s)
                       Enter MET TIME (HH:MM:SS):      04:30:00 MET

                       Press ENTER to accept, SPACE BAR to repeat: _

   The sample above shows the screen after the day and time entries have been 
   completed. The Mission Elapsed Time is immediately converted to actual date 
   and time and the current SIMULATED date and time, based upon the MET just 
   entered, are then displayed (and counting) for approval. Press ENTER to 
   accept the time and date displayed, or press the SPACE BAR to repeat the 
   entries.
        Press ENTER to return to the Main Menu with the date and time as 
   displayed on the screen (Current or Simulated).


   F9     DOS Shell (CAUTION: DOS Version 3.x ONLY!)
   -------------------------------------------------

        If a system function is desired at the Main Menu, press F9 to execute 
   QuickBASIC's DOS SHELL function. This will return you to a DOS prompt and 
   most DOS commands may be executed immediately. When the Shell is executed, 
   STSORBIT remains in memory and the map data will not be re-read when you 
   return. However, this means that a substantial amount of memory is in use 
   and not available to DOS during the shell operations. Enter "EXIT" (without 
   the quotation marks and followed by ENTER) at the DOS prompt when you wish 
   to return to STSORBIT. 

        CAUTION: The QuickBASIC SHELL function is only reliable for versions 
        of DOS of 3.0 or higher! Systems with less than 640K memory may fail 
        to execute the shell and applications requiring large amounts of 
        memory may also fail.

   F10    Set STSORBIT Program Options and Features
   ------------------------------------------------

        A number of program features and display options are set using the F10 
   Program Options Menu. These selections are further described in the section 
   "Program Options Menu" below.


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 22


   ENTER  Resume Mission
   ---------------------

        Pressing ENTER resumes the current mission shown in parentheses to the 
   right of the command on the Main Menu. The 2-line elements file from which 
   the data was read is shown in square brackets.

            ENTER  Resume Mission                  (STS-41 [STS41F])

   Any manually entered data is retained. "ENTER" means the key marked ENTER, 
   RETURN, or with a left pointing arrow -- but not the backspace or cursor 
   position keys which may also be marked with arrows! (I am afflicted with 
   too long a memory; once upon a time this function was known as Carriage 
   Return and was often shortened to RETURN or even CR. With the advent of 
   electronic typewriters, video terminals, dot matrix printers and all the 
   rest, "Carriages" have long since disappeared but old habits die hard! Most 
   PC keyboards are now marked with "ENTER".)
        Use ENTER to resume plotting a mission in progress after returning to 
   the Main Menu to perform some change (such as enabling the node display, 
   enabling the NASA tracking stations, or adjusting the time or date).


   ESC    Quit STSORBIT and Save Current Mission
   ---------------------------------------------

        Press ESC (the key marked "ESC" or "Esc", not the letters E+S+C) to 
   quit program STSORBIT. If you press ESC to quit the program and have 
   manually entered orbital data, STSORBIT will save all required mission data 
   in file STSORBIT.INI prior to terminating. This will be the data available 
   with the ENTER key the next time you execute the program. The demonstration 
   data will not be saved, preserving any previously saved mission data.
        When you have finished with STSORBIT, press ESC at the Main Menu to 
   return to DOS. The data (and any adjustments you have made) for the current 
   mission are saved in file STSORBIT.INI, but the map data is lost and will 
   be re-read when you next use program STSORBIT. NOTE: If you have neither 
   entered data (with the E command) nor read a previously saved .INI file 
   (with the F command), no data will be saved when you exit STSORBIT.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 23


   PROGRAM OPTIONS AND FEATURES MENU
   ---------------------------------

        A number of program features and display options are set using the F10 
   Program Options Menu. When used with CGA displays, the features shown below 
   as selected by function keys F3 and F4 are not available because of the low 
   resolution of the CGA display. The following Options Menu is displayed when 
   the F10 command is entered from the Main Menu:


                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:35:25 PDT   23:35:25 UTC
                      Current date:    05/21/1991     05/21/1991


            F1             Program STSORBIT Information
            F2             Set New Local Coordinates (Calaveras County, CA)
            F3             Select Display Features
            F6     USA     Set Map Center (USA/Europe)
            F7     OFF     Set for SLOW COMPUTER or NO COPROCESSOR
            F9    -7.00    Set UTC Time Offset and Daylight Flag
            F10    OFF     Enable/Disable Printer Logging

            ENTER          Return to MAIN MENU

            Select desired function:



   F1     Program STSORBIT Information
   -----------------------------------

        Function Key F1 displays information about program STSORBIT including 
   the copyright notice, version number, my name and address, and the 
   telephone number of my RPV ASTRONOMY BBS (Bulletin Board System). The 
   current version of STSORBIT is always posted on the BBS. The BBS has a 
   power controller; if it hasn't answered after the THIRD RING, hang up and 
   call back in two minutes. The BBS is available 24 hours per day at 2400 and 
   1200 baud.


   F2     Set New Local Coordinates
   --------------------------------

        In order to perform the calculations related to satellite visibility 
   and altitude/azimuth, STSORBIT must know the geographic coordinates for the 
   user's location. The name of the current location is shown in parentheses. 
   When STSORBIT is first started, the default coordinates are set to Rancho 
   Palos Verdes, California, near Los Angeles. The current location is 
   indicated by the name in parentheses on the Options Menu. The program 
   provides two methods for setting your own coordinates: reading a file of 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 24


   city names and coordinates (STSORBIT.CTY); or manually entering the 
   information.
        Pressing F2 will display the following reminder:

        STSORBIT will search for the CITYNAME you enter anywhere in the city 
        names in the file. For example, 'SAN' appears in 'SAN FRANCISCO', 'SAN 
        DIEGO', 'SANTA ANA', 'THOUSAND OAKS', etc. Press ENTER to cancel the 
        search or enter '*' to enter a new city name and coordinates.

        In other words, when you enter a name or partial name, STSORBIT will 
   attempt to match that group of characters anywhere in the names which 
   appear in the city file. For example, 'SAN' matches 'SAN diego' as well as 
   'SAN jose' and 'thouSANd oaks'. To get 'SAN FRANCISCO' on the first try, 
   enter 'SAN F' with a space between the 'N' and 'F'. Case is not 
   significant; upper and lower case letters are treated identically. If you 
   change your mind and wish to cancel the operation, simply press ENTER by 
   itself. Use BACKSPACE to make corrections.
        To begin the search, enter the desired name after the prompt. In the 
   example which follows, the name 'ran' was entered for the search.

        Enter CITYNAME to search for:  ran

        Processing record  1
          City Name:  Rancho Palos Verdes CA
          Latitude:     33.7675
          Longitude:  -118.4033
          Elevation:   186 meters

        Press ENTER to ACCEPT this city as your location, OR
        Press TAB to also display this city's location, OR
        Press SPACE to search for next city:  _

        If the city displayed is the one you wish to use as your local 
   coordinates, press ENTER. If you wish to display this city as a second 
   location on the display, press TAB. The data will be entered into STSORBIT 
   and subsequently saved in file STSORBIT.INI. If you wish to search further 
   in the file, press the SPACE BAR.

        NOTE: The elevations contained in file STSORBIT.CTY are almost all 
        zero except for Rancho Palos Verdes, CA and Calaveras County, CA, 
        locations for which I have accurate elevations above mean sea level. 
        If you know the correct elevation, edit the file using any ASCII text 
        editor and change the last number on the line. STSORBIT.CTY contains 
        over 800 cities and uses a different format than the .CTY files for 
        program ASTROCLK (the elevation has been added to each entry). If 
        users send me their correct elevations (or additional cities they wish 
        added), I will incorporate that data into subsequent versions of file 
        STSORBIT.CTY.

        To enter location data manually, press "*" (without the quotation 
   marks) followed by ENTER. You will be prompted for the city name, latitude, 
   longitude, and elevation. Latitude and longitude may be entered using three 
   different formats for convenience (note the use of comma and decimal 
   point):


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 25


             DDD.DDDDD           Degrees and decimal fraction
             DD,MM.MMM           Degrees, minutes and decimal fraction
             DD,MM,SS.SS         Degrees, minutes, seconds and fraction

   Note that SOUTH latitude and WEST longitude must be entered as NEGATIVE 
   numbers as measured south of the equator or west of Greenwich, 
   respectively. The default unit for elevations is meters above mean sea 
   level; add "F" (upper or lower case without the quotation marks) if you 
   wish to use feet.
        After the elevation has been entered, the data will be displayed for 
   approval. All data are converted to degrees or meters as appropriate, 
   regardless of the units used on input.

          City Name:  Rancho Palos Verdes CA
          Latitude:     33.7675
          Longitude:  -118.4033
          Elevation:   186 meters

        Press ENTER to ACCEPT this city, OR
        Press SPACE to cancel this data:  _

   Press ENTER to accept the data as shown or SPACE to cancel the data and 
   return to the Options Menu. If the data is accepted, STSORBIT will ask if 
   you wish to append (add) this city/location to the existing file 
   STSORBIT.CTY so that it will be automatically available thereafter.

        Do you with to append this data to file STSORBIT.CTY (Y/n):  _

   Press "Y" or ENTER to append the data to the file, or press "N" to not 
   modify the STSORBIT.CTY file.


   F3     Set Display Features
   ---------------------------

        A number of display features may be enabled or disabled using a 
   separate sub-menu. See complete description below.

   F6     Set Map Center (USA/Europe)
   ----------------------------------

        The F6 command changes the center of the displayed world map. By 
   default, the map is centered on the United States at 90 degrees West 
   longitude. Most Americans are accustomed to viewing the map in that 
   orientation, but it is sometimes convenient to shift the map center when 
   the Space Shuttle is near the edge of the map. If you prefer to have the 
   map centered at the prime meridian or zero degrees (Greenwich, England), 
   use the F6 command or use the /EUR command line option when starting 
   STSORBIT. Each time you use the F6 command the map center is changed to the 
   alternate meridian and the map data is re-read from disk.



   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 26


   F7     Set for SLOW COMPUTER or NO COPROCESSOR
   ----------------------------------------------

        IMPORTANT NOTE:     ALWAYS select the Slow Mode if your computer is 
                            not equipped with a math coprocessor.

        Particularly since the addition of the calculations related to 2-line 
   element sets, it has become increasingly difficult for very slow computers 
   or computers not equipped with a math coprocessor to keep up with real time 
   orbital calculations being performed by STSORBIT. For example, my vanilla 
   Zenith Z-148, operating at 4.77 MHz and no math coprocessor, takes 
   approximately 4.5 seconds to make a full set of orbital position 
   calculations; when switched to 8.0 MHz, the same calculations require only 
   2.5 seconds. In either case, the program gets hopelessly behind itself and 
   can never catch up when operated in the normal program mode.
        While perhaps not the "ideal solution" as compared to having a math 
   coprocessor, setting STSORBIT for Slow Mode can help in all but the most 
   severe cases. Instead of attempting to update its position calculations 
   every second, the update is slowed to every five seconds in this mode. This 
   allows the computer to more or less keep up at a cost of not having data 
   quite in real time on a second-by-second basis. Except for the frequency of 
   updates, all program features are unchanged. When STSORBIT is operating in 
   the Slow Mode, the phrase "SLO" appears at the lower right of the tracking 
   display.
        Since STSORBIT makes no test to see if it is keeping up with real time 
   (the program cannot tell the difference between the PAUSE or SIMULATED TIME 
   modes versus REAL TIME) and since most features are available for all 
   computer configurations, it is the responsibility of the user to make sure 
   that the appropriate options have been selected. Even in the Slow Mode, 
   certain very slow computers (such as an old XT-class computer running at 
   4.77 MHz) cannot keep up if the solar terminator is enabled when using the 
   2-line elements orbital data.


   F9     Set UTC Time Offset and Daylight Flag
   --------------------------------------------

        STSORBIT uses UTC or Coordinated Universal Time, an adjusted version 
   of Universal Time (which STSORBIT considers the same as GMT or Greenwich 
   Mean Time), for certain functions such as launch time. The difference 
   between UT, UT1, UT2 and UTC is never more than 0.9 seconds. UTC is used 
   because it is the standard for civil timekeeping and agrees with standard 
   atomic time, TDB or Terrestrial Barycentric Time, used by astronomers. 
   However, NASA continues to use the GMT designation, a holdover from earlier 
   days before the introduction of UTC. Using UTC permits critical data to be 
   used across many time zones without conversion. However, it also means that 
   STSORBIT must know what number of hours to add to UTC in order to obtain 
   your local time, and whether or not you are currently using daylight 
   savings time (summer time in the UK).
        When prompted, enter the time offset in hours from your local time to 
   Coordinated Universal Time. Examples are shown for most time zones in North 
   America. STSORBIT then asks if you are using daylight savings time; enter 
   "0" if not, and "1" if so. The sum of these two values is shown on the Main 
   Menu; for example, if the computer is set to Pacific Daylight Time (UTC 
   offset is -8.00 hours and Daylight Flag = 1), the sum will be -7.00. For 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 27


   most time zones in North America, the correct zone abbreviation will be 
   shown on the ground track display for Local date and time. When you change 
   your computer from/to daylight savings time, use this command to update 
   STSORBIT. The following shows the display when using the F9 command:


   Set UTC TIME ZONE OFFSET and DAYLIGHT FLAG

             STSORBIT must know the difference between your local time zone 
        and Coordinated Universal Time (UTC), also sometimes known as 
        Greenwich Mean Time (GMT). With this information, STSORBIT can 
        automatically adjust launch or Epoch times and dates for your local 
        time zone. In addition, STSORBIT must know if your computer is now set 
        to STANDARD or DAYLIGHT time.
             First, enter the difference between your STANDARD time zone and 
        UTC in hours. Do NOT include the hour for daylight time if you are now 
        on DAYLIGHT time; it will be entered separately. For most time zones 
        in the United States and Canada, the entries required are:

             Eastern Standard Time     EST    -5.0
             Central Standard Time     CST    -6.0
             Mountain Standard Time    MST    -7.0
             Pacific Standard Time     PST    -8.0

             Enter UTC Offset (hours):          -8
             Enter DAYLIGHT Flag (0=OFF, 1=ON): 1


        Once this information has been entered, it will be saved in file 
   STSORBIT.INI and will not be requested again. If you change from Standard 
   to Daylight Time or vice versa, use the F10+F9 command to update the 
   Daylight Flag. INI files obtained from other users may be from a prior 
   version of STSORBIT and the time information may have to be corrected.


   F10    Enable/Disable Printer Logging
   -------------------------------------
        I have found it interesting to log the orbital data and the ascending 
   and descending node information on my printer when analyzing the mission 
   data over long periods of time. The F10 command toggles the printer logging 
   function on and off. The first page of the log includes the current orbital 
   data and subsequent pages contain only node information. In addition to the 
   information presented on the display, the printer log also calculates the 
   current orbital time, the time from one ascending (descending) node to the 
   next. A typical log is shown below. 

        IMPORTANT:     BE SURE THE PRINTER IS TURNED ON PRIOR TO ENTERING THE 
                       F10 COMMAND. 

   STSORBIT: Space Shuttle Tracking Program, Version 9122          Page 1

   ORBITAL DATA for STS-31 Discovery/HST

             Launch Date:             04/24/1990
             Launch Time:             05:33:52

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 28


             Orbit Inclination:       28.4695
             Orbit Altitude:         329.50 nm

             Adjust Longitude:         9.80
             Adjust Orbit Time:        8.40 min

                                                                  ORBITAL
   LOCAL DATE      TIME              ORBIT    LONG           MET     TIME
   04/28/1990  20:32:52  Ascend Node:   70  -69.95    4/14:58:07  1:36:55
   04/28/1990  21:20:52  Dscend Node:   70   97.64    4/15:46:35  1:36:55
   04/28/1990  22:09:52  Ascend Node:   71  -94.77    4/16:35:02  1:36:55


        When printer logging is enabled and the ground track is displayed, the 
   word "LOG" will appear in red at the right of the text area. Enabling 
   printer logging also automatically enagles the display of ascending and 
   descending node information.
        When a printer log is prepared for 2-line orbits, the Adjust Longitude 
   and Adjust Orbit Time entries will not be shown in the header data. The 
   Launch Date and Launch Time entries are given if that information has been 
   entered indepentently. The Epoch Date and Epoch Time are always shown for 
   2-line element simulations. Note also that the orbit altitude shown is the 
   altitude at the time the log was started and will not be correct for 
   subsequent entries, especially if the satellite has an elliptical orbit 
   (high eccentricity).
        A printer log may be prepared in advance of a mission by enabling 
   printer logging from the Set Options Menu (with the F10+F10 command), 
   setting the desired simulation time (F8+F3 command), then starting the 
   ground track display with ENTER; once the ground track has appeared on the 
   screen, pressing the F key twice to set STSORBIT in the X60 fast time mode 
   will generate the date relatively quickly (although the UT TIME printed may 
   be off by as much as one minute in the X60 mode). Allow the simulation to 
   run for the desired length of time, then press ENTER to return to the Main 
   Menu. While the ground track is active Function Key F3 performs the same 
   function as the F10+F10 command to enable or disable printer logging.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 29


   SET DISPLAY FEATURES
   --------------------

        Depending upon the satellte and personal preferences, a variety of 
   display features may be enabled or disabled. Not all features are available 
   with monochrome or CGA monitors. Pressing F3 on the Set Program Options and 
   Features Menu will display the following menu:

                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9122

                      Current time:  16:35:52 PDT   23:35:52 UTC
                      Current date:    05/21/1991     05/21/1991


            F2     ON      Display TDRS Coverage
            F3     OFF     Display Additional Map Grid Lines
            F4     OFF     Display NASA Tracking Stations
            F5     OFF     Show Ascending & Descending Node Data
            F6     ON      Display Spacecraft Circle of Visibility
            F7     ON      Display South Atlantic Anomaly Zone
            F8     ON      Display Terminator, SUN, and Spacecraft Lighting
            F9     NM      Select Distance Units: NM or KM
            F10    A/A     Select Satellite Coordinates: RA/DEC, Alt/Az or XYZ

            ENTER          Return to MAIN MENU

            Select desired function:

   F2     Display TDRS Coverage
   ----------------------------

        This command will display the approximate communications coverage for 
   the Tracking and Data Relay Satellites (TDRS) EAST and WEST. The coverage 
   boundaries overlap between the East and West TDRS satellites and Mission 
   Control may select either satellite during the overlap period. STSORBIT 
   assumes, as is often the case, that TDRS East will be selected when it is 
   available.

   F3     Enable/Disable Additional Map Grid Lines
   -----------------------------------------------

        This command is not available for CGA systems. The basic world map 
   includes the equator and the meridians at 0 degrees, 90 degrees, and -90 
   degrees shown in blue on color monitors; the equator and the prime meridian 
   are shown in bright blue. Turning on the map grid adds lines of longitude 
   every 30 degrees and lines of latitude every 10 degrees. Displaying the 
   additional grid lines on monochrome monitors usually makes the screen too 
   "busy" and is not recommended.


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 30


   F4     Display NASA Tracking Stations
   -------------------------------------

        The F4 command enables/disables the display of NASA's 14 ground 
   tracking stations; this command is not available for CGA monitors. For 
   additional discussion, see the section Ground Track Display.

   F5     Show Ascending & Descending Node Data
   --------------------------------------------

        The nodes of an Earth orbit are the points on the ground track where 
   the path crosses the equator. The ascending node crosses from South to 
   North and the descending node crosses from North to South. Orbit numbers 
   normally increment at the ascending node. This command adds two additional 
   lines of data at the lower left of the screen giving the time (MET or time 
   since epoch) and longitude of the most recent ascending and descending 
   nodes. This information is useful when comparing STSORBIT's data against 
   other sources such as the wall map in Mission Control.

   F5     Display Spacecraft Circle of Visibility
   ----------------------------------------------

        STSORBIT can calculate the approximate circle of visibility from the 
   spacecraft, the area of the Earth's surface which is visible from the 
   cockpit windows and television cameras or, for unmanned spacecraft, the 
   direct line of sight visibility from the ground. Beginning with Version 
   9123, this feature may be enabled for all spacecraft using 2-line elements. 
   When the program is run in the normal mode, the circle of visibility is 
   recalculated every 10 seconds based upon the spacecraft's current altitude. 
   This means that orbits with a high eccentricity (that is, a highly 
   elliptical orbit whose apogee and perigee are very different) will exhibit 
   a constantly changing circle of visibility. When the program is run in the 
   Slow Mode, the radius of the circle of visibility is constant, as 
   calculated at the moment the ground track display is started. This feature 
   may also be enabled or disabled during the ground track display using 
   Function Key F7.

   F7     Display South Atlantic Anamoly Zone
   ------------------------------------------

        The South Atlantic Anamoly (SAA) is an area in the southern hemisphere 
   lying between southern tip of Africa and South America which can cause 
   severe electromagnetic disturbances on spacecraft. For example, the 
   semiconductor memory on the Hubble Space Telescope (which regularly passes 
   through the SAA) was being changed by this phenomenon until a patch was 
   uplinked to work around the problem. The area is shown on the ground track 
   as an ellipse for simplicity; its actual outline is more nearly shaped like 
   a kidney bean and varies somewhat with spacecraft altitude.

   F8     Display Terminator, Sun, and SpaceCraft Lighting
   -------------------------------------------------------

        Many types of observations, especially Earth observations, often 
   require that the target or terrain be in sunlight. The solar terminator is 
   a series of yellow points on the display which represent the line at which 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 31


   the center of the Sun is at an observer's horizon for mean sea level. 
   Although a quick glance outside should suffice to determine which side of 
   the terminator line is in sunlight and which in darkness, EGA and VGA 
   systems also display the Sun as a small yellow circle. The terminator is 
   partially updated every 10 seconds (and is fully updated every 60 seconds) 
   and the sun is updated every 60 seconds. Because of the additional 
   calculations and plotting required, these solar features may not be 
   suitable for slow processors or computers without a math coprocessor. NOTE: 
   Only the terminator is available with CGA systems.
        The terminator is sometimes confused with a line denoting sunrise and 
   sunset. Two factors make the terminator only an approximation: first, the 
   terminator is based upon the center of the Sun, while sunrise and sunset 
   are based upon the upper limb of the Sun; and second, the terminator is 
   calculated for mean sea level rather than a specific local elevation. These 
   two factors combined can result in a difference of ten minutes or more when 
   the times are compared against published values or those calculated by my 
   program ASTROCLK, sunrise being earlier and sunset being later.
        The performance of solar panels and certain other instruments on a 
   spacecraft is dependent upon whether or not the Sun is in view. Similarly, 
   it is usually impossible to visually see a spacecraft which is not in 
   sunlight. STSORBIT calculates whether the spacecraft is in full sun, 
   penumbra/refracted sunlight, or umbra (full shadow) and adjusts the color 
   of the spacecraft icon accordingly: white, yellow, and bright white 
   respectively. This feature is not available on CGA and HGC monitors.

   F9     Select Distance Units: NM or KM
   --------------------------------------

        Spacecraft altitude, range, and satellite geocentric rectangular 
   coordinates (X, Y, and Z) may be expressed in either nautical miles (nm) or 
   kilometers (km). This feature selects which units will be displayed for 
   those data. You may also use Function Key F9 while the ground track display 
   is in progress to switch between units of distance measure.

   F10    Select Satellite Coordinates: RA/DEC, AltAz or XYZ
   ---------------------------------------------------------

        This feature selects between topocentric (referenced to the Earth's 
   surface and in this case the current local geographical coordinates) 
   horizon, equatorial coordinates for the satellite's position (Right 
   Ascension and Declination), or geocentric rectangular coordinates (X, Y, 
   and Z, referenced to the center of the Earth). Press F10 until the desired 
   coordinate system is selected. The abbreviations "R/D", "A/A", and "XYZ" 
   are used on the menu. You may also use Function Key F10 to switch between 
   coordinate systems while the ground track siaplay is in progress. NOTE: The 
   geocentric rectangular coordinates are only available when using 2-line 
   orbital elements.
        For most purposes, such as aiming an antenna or visually spotting the 
   satellite, the horizon coordinates of Altitude and Azimuth are desired. If 
   you wish to determine the star background, however, the equatorial 
   coordinate system of Right Ascension and Declination (referenced to the 
   epoch of date) is needed. For both of these coordinate systems, the range 
   from the current local coordinates to the satellite is also given, 
   expressed in either nautical miles or kilometers as selected by F9 above.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 32


   USING GROUND TRACK DISPLAY OPTIONS
   ----------------------------------

        Once the orbital display is in progress, a number of keys are active:

           ENTER  Return to Main Menu (cancel this simulation).

              F1  On-line HELP. Press F1 to display a help screen in the lower 
                  portion of the screen. Press F1 again to resume normal data 
                  display.

              F2  Toggle the BLINK mode of the space shuttle or satellite 
                  symbol between blinking and steady.

              F3  Enable or disable printer logging. If logging is enabled, 
                  the word LOG appears in the lower right of the screen. Be 
                  sure the printer is turned on BEFORE using the L command. 
                  The "L" command automatically enables the display of 
                  ascending and descending node information.

              F4  Toggle FAST mode from x1 to x10 to x60 to x1, etc. When 
                  either of the fast modes is enabled, "(x10)" or "(x60)" will 
                  appear at the upper right of the data block in red. This 
                  feature operates in both the normal (real or simulated time) 
                  and PAUSE modes.

              F5  When using 2-line elements, the elapsed time may be switched 
                  between "T+Epoch" and "MET" by using the "T" command. If no 
                  launch time and date have been entered, the "T" command will 
                  have no effect.

              F6  Enable/Disable PAUSE mode; only the local date and time are 
                  updated. The plot is frozen at the current position and the 
                  "+" and "-" commands are enabled.

              F7  Enable or disable the spacecraft circle of visibility.

              F8  Enable or disable the SUN, solar terminator, and spacecraft 
                  lighting feature. NOTE: The SUN and spacecraft lighting are 
                  not available on CGA systems.

              F9  Change units of distance between kilometers (km) and 
                  nautical miles (NM).

             F10  Change satellite coordinates between Altitude and Azimuth, 
                  Right Ascension and Declination, and Geocentric Rectangular 
                  (XYZ) systems.

               +  During PAUSE mode only, moves the satellite to the NEXT 
                  calculated position based upon the FAST mode then in effect: 
                  simulated time is advanced 1, 10, or 60 seconds. (NOTE: The 
                  "=" key may be used instead of "+" to avoid the SHIFT KEY.)

               -  During PAUSE mode only, moves the satellite to the PREVIOUS 
                  calculated position based upon the FAST mode then in effect: 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 33


                  simulated time is backed up 1, 10, or 60 seconds.

                  NOTE: Since this "-" or reverse feature was implemented 
                  primarily for testing and demonstration, the ground track 
                  logic does not recognize these reverse movements and will 
                  become slightly confused. To restore the ground track and 
                  current times properly, press ENTER TWICE to stop the 
                  display and then to resume the mission.

               R  Resynchronize MET or T+Epoch with Local Time. Resets plot to 
                  real time.

                  NOTE: The Resynchronization was feature was originally 
                  intended only for testing and should only be performed when 
                  the simulated time and local times are reasonably close to 
                  each other. The plot may otherwise have some extraneous 
                  pixels left around! This feature has not been extensively 
                  tested. To restore the ground track completely, press ENTER 
                  to stop the display and return to the Main Menu, then press 
                  ENTER again to resume the mission.

        The simulated time, taking into account any fast time that may have 
   been in effect up to that point, is shown at the lower left of the screen. 
   For reference, the launch or epoch time and the actual local time (as 
   determined by the computer's internal DOS clock) are also displayed. The 
   MET (Mission Elapsed Time) or T+Epoch display at the lower right of the 
   screen shows the current elapsed time in the mission and will include an 
   additional message, "(x10)" or "(x60)", when fast time is in effect.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 34


   THE STSORBIT GROUND TRACK DISPLAY
   ---------------------------------

        One of the principal objectives of STSORBIT is to graphically display 
   the position of the space shuttle or satellite relative to a map of the 
   world. In addition to the map itself, a number of other items of interest 
   are displayed. Some features are available only with higher resolution 
   displays (EGA and VGA) in order to avoid cluttering the display screen. 
   Other features may be enabled or disabled according to the user's 
   preference. The following sections discuss these various features.


   On-line Help
   ------------

        Thanks to numerous suggestions, an on-line help screen may be 
   displayed during the ground track display to remind the user of the 
   available functions and which keys to press to trigger those functions. 
   When the ground track display is active, press Function Key F1 to display 
   the following help information in the lower portion of the screen.

    F1  Resume Data          F6  Pause Display ---------+ During PAUSE:
    F2  Satellite Blink      F7  Circle of Visibility   | +  Move Forward
    F3  Printer Logging      F8  SUN and Terminator     | -  Move Backward
    F4  Time Step            F9  Distance Units
    F5  MET/T+Epoch         F10  Satelitte Coordinates       STSORBIT

        The ground track display will continue to be updated in real time 
   while the help screen is displayed. If only the graphical display of the 
   ground track is of interest, the help screen may be kept on the display 
   continuously. Press Function Key F1 again to return to the normal data 
   display in the lower portion of the screen.
        Versions prior to 9122 used various letter keys to select the various 
   functions during the ground track display. I have switched to the function 
   keys in an attempt to better organize these operations.


   World Map
   ---------

        The STSORBIT ground track display includes a map of the world centered 
   on either the United States or Europe and extending from approximately +80 
   degrees North latitude to -80 degrees South latitude using a linear 
   cylindrical projection. Omitting the two 10 degree bands at the poles 
   permits better detail in the mid latitudes where all space shuttle orbits 
   and many other satellite orbits are concentrated. Ground track details very 
   near the poles are therefore sacrificed for a better display in the main 
   portion of typical orbits. The vertical resolution of the display is 
   automatically adjusted for the type of display system in use from 200 lines 
   (CGA) to 480 lines (VGA).
        The world map consists of a series of some 7500 coordinate pairs. The 
   equator and lines of equal longitude at 0, 90, and -90 are also shown. 
   Additional lines of longitude and latitude may be added on EGA and VGA 
   monitors by enabling that feature using F10+F3+F3. When used with an EGA or 
   VGA color monitor, the coastal outlines are in cyan, the equator and 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 35


   longitude grid are in blue with the equator and Prime Meridian highlighted 
   in bright blue.


   Spacecraft or Satellite and Orbit Projections
   ---------------------------------------------

        The focus of the display, and the reason for program STSORBIT, is to 
   show the position of the spacecraft or satellite. For the space shuttle 
   (and provided the mission name begins with the letters "STS"), a symbol has 
   been chosen which resembles that spacecraft. For all other satellites, a 
   symbol has been chosen which resembles the Hubble Space Telescope. In 
   either case, the symbol is shown in the following colors (EGA and VGA 
   displays only):

             Satellite is sunlit           Light White
             Satellite is in penumbra      Yellow
             Satellite is in umbra         White

   For better visibility, the symbol will normally "blink" on CGA monitors; 
   the symbol may be made to blink on any system if desired by pressing the 
   "B" key while the ground track is displayed.
        Just seeing the spacecraft or satellite on the map display yields 
   information as to its present position. However, for satellite viewing and 
   planning purposes, STSORBIT calculates the predicted orbital ground track 
   for approximately three hours in the future and displays the past orbital 
   ground track for approximately one and a half hours in the past. The future 
   ground track is shown in light green, and the past orbital ground track is 
   shown in light red.
        The orbital ground track consists of a series of dots plotted at one 
   minute intervals. These dots "move" as the spacecraft or satellite changes 
   position; one new dot is added to the predicted track each minute and one 
   dot is removed from the past track at the same time.


   User's Circle of Visibility
   ---------------------------

        Centered around the user's geographic location, and marked with a 
   small cross on EGA and VGA systems, is a magenta "circle" of the 
   approximate line of sight visibility for the mission in progress. The 
   circle appears on the display as an ellipse because of the scaling factors 
   used by the map projection. The radius of this circle of visibility is 
   calculated for each satellite based upon its altitude at the instant the 
   map is drawn as well as the user's elevation above mean sea level and 
   corresponds to "line of sight" visibility for that satellite.
        When a satellite is within the circle, direct visual, radio or radar 
   communications with the satellite should be practical. Actual visibility, 
   of course, depends upon more than simply whether or not the satellite is 
   above the viewer's horizon. Most important is the sun to satellite to 
   viewer geometry; the satellite must be in sunlight and the viewer in 
   darkness for reasonable visibility. Almost as important is the size and 
   geometry of the satellite itself; a large, bright-metal satellite with huge 
   solar arrays reflects far more sunlight than a small dark satellite. In 
   addition to the satellites themselves, many booster rockets and other 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 36


   "spare parts" are orbiting the Earth. Since they are not attitude 
   stabilized, booster rockets usually are tumbling and may therefore appear 
   to flash on and off as they pass over.
        For the Space Shuttle as well as most other satellites with near 
   circular orbits, the circle of visibility calculations are reasonably 
   accurate; however, the position of the sun and the effect of atmospheric 
   refraction are not taken into account, only whether or not the satellite is 
   in line of sight view from the observing location. For highly eliptical 
   orbits, however, the accuracy is substantially degraded since the radius of 
   the circle of visibility changes dramatically depending upon whether the 
   satellite is nearer apogee or perigee at the time the calculation is made, 
   and the period of the orbit. In the course of a single orbit, the altitude 
   of such a satellite may change by thousands of miles. Satellite "DE 1", 
   usually included in the NASAnnn.TXT 2-line elements file, is in a highly 
   elliptical orbit with long period and illustrates the problem.


   Spacecraft Circle of Visibility
   -------------------------------

        The spacecraft circle of visibility is calculated using the same 
   alrorithm as for the user's circle of visibility. Like the user's circle, 
   the spacecraft circle appears on the display as an ellipse because of the 
   scaling factors used by the map projection. The difference is that the 
   spacecraft circle moves with the spacecraft and illustrates the approximate 
   area visible from the spacecraft at any given moment. The circle is updated 
   at the same rate as the spacecraft symbol, normally every ten seconds. 
   Comparisons with a VGA display system during the STS-35/ASTRO-1 mission in 
   December, 1990 confirmed that the circle shown is quite close to that shown 
   by one of the special graphics displays occasionally shown on NASA Select 
   TV.


   TDRS Satellite Features
   -----------------------

        TDRS Satellite features are shown only on HGC, EGA and VGA monitors. 
   The three TDRS satellites (Tracking and Data Relay Satellites), used for 
   most communications to and from the Space Shuttle and the Hubble Space 
   Telescope, are each shown as a dot inside a small yellow circle on the 
   equator. There are three TDRS satellites in geosynchronous orbit, TDRS East 
   at approximately 72 degrees West longitude and the TDRS West Cluster 
   consisting of two satellites at approximately 170 degrees West longitude. 
   Both of the TDRS West Cluster satellites have partially failed but between 
   them they can provide the facilities of a fully operational satellite.
        Each TDRS location provides communications coverage for almost half of 
   the Earth. However, since the ground station is at White Sands, New Mexico, 
   the coverage overlaps to provide good communications. This, in turn, means 
   that there is a narrow band, known by NASA as the Zone of Exclusion, off 
   the East coast of Africa which is not covered by either TDRS. Four slightly 
   curved vertical red lines on the display show the limits of coverage for 
   each TDRS location. With the map centered on the United States and scanning 
   from left to right, the red coverage lines are acquisition of TDRS East, 
   loss of TDRS West, loss of TDRS East, and acquisition of TDRS West.
        During most of an orbit, the satellite being used for communications 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 37


   will be shown in the data block opposite the title "Com:"; the messages 
   "TDRS-West" or "TDRS-East" will appear. Approximately five minutes before 
   the spacecraft reaches loss TDRS East, the message will change to "LOS 
   5:07" with the numbers indicating the minutes:seconds until anticipated 
   signal loss. Once the signal is lost, the message will change to "AOS 7:35" 
   to show the time remaining until acquisition by TDRS West. The algorithm 
   used for the calculation of the TDRS coverage is very approximate but is 
   usually accurate to within approximately 30 seconds.

   NASA Ground Tracking Stations
   -----------------------------

        NASA maintains a number of ground tracking stations around the world. 
   Some of these tracking stations are essential for the ascent or landing 
   phases of a space shuttle flight; others are used for in-flight 
   communications. Each ground tracking station is shown as a small symbol 
   surrounded by a brown or light yellow "circle" which gives the approximate 
   area of antenna coverage and shows how small a proportion of each orbit can 
   be monitored without the TDRS system. When for some reason the TDRS system 
   is down (as has occurred during infrequent computer failures at White 
   Sands, New Mexico, the TDRS Ground Station), these ground tracking stations 
   become the only means of communication with the Space Shuttle. Because of 
   budget constraints, many of these ground tracking stations may be (or have 
   already been) shut down. Some, such as MIL and BDA (see list below) will be 
   retained because they are required for the ascent phase of a space shuttle 
   mission. Others, such as HAW, CTS and GWM, are operated jointly with, or 
   independently by, the U. S. Air Force.
        The antenna range circle is displayed on the screen as an ellipse 
   because of the scaling factors used by the map projection. For all systems 
   except CGA, the locations of the three TDRS (Tracking and Data Relay 
   Satellite) are shown as small circles on the equator at -41 degrees and at 
   -171 degrees; on CGA displays the TDRS coverage is NOT shown in order to 
   avoid confusing the display. The following table lists the ground tracking 
   stations as of early 1989 which are shown along with their abbreviations 
   and approximate map coordinates (longitude, latitude):

             MIL     -81,28       Merritt Island, FL
             BDA     -64,32       Bermuda
             DKR     -17,14       Dakar, Senegal
             ACN     -14,-8       Ascension Island
             MAX     -5,41        Central Spain
             IOS      56,-5       Indian Ocean
             HAW     -156,20      Hawaii
             GWM      145,14      Gwam
             VAN     -122,35      Vandenberg, CA
             YAR      115,-29     Yargidy, Australia
             CAN      149,-36     Canberra, Australia
             GDX     -116,34      Goldstone, CA
             CTS     -105,38      Colorado Springs, CO
             AGO     -71,-34      Santiago, Chile

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 38


   STSORBIT'S ORBITAL MODELS
   -------------------------

        The initial version of STSORBIT was prepared without reference 
   materials of any kind and the simplest possible orbital model was therefore 
   selected. The primary objective was to duplicate the NASA wall map at 
   the Mission Control Center in Houston, Texas. This "simple" model assumed 
   that the orbit was perfectly circular at a specified altitude and 
   inclination which never degraded due to other factors such as drag or 
   perturbation. Some simplifying assumptions were incorporated to handle the 
   initial ascent portion of a mission and the launch site was hard coded to 
   Cape Canaveral, Florida. With only minor modifications, the program was 
   essentially unchanged for the next year.
        The launch of STS-31 and the Hubble Space Telescope highlighted the 
   need for improved accuracy because of public interest and the length of the 
   mission. The orbital calculations were modified (STSORBIT Version 9015) to 
   include the J2 factor, the perturbation of low Earth orbits due to 
   variations in the gravitational field related to the non-spherical shape of 
   the Earth (among other factors); omission of the J2 factor caused errors in 
   longitude of approximately -5 to -7 degrees per day. That is, the orbital 
   track drifted Westward from its true position by that amount. More accurate 
   models of low orbits also include the J3 and J4 perturbation factors, 
   atmospheric drag, and a host of other less significant items.
        Although by now reasonably accurate for the first day or so of a space 
   shuttle mission, the "simple" model is by no means ideal. In calculating 
   the current orbital longitude, for example, the "simple" model assumes a 
   circular orbit with an orbital inclination of zero degrees. For orbits with 
   low inclinations, as is typical for launches from Kennedy Space Center, 
   these errors are not particularly significant and are probably overshadowed 
   by the fundamental uncertainties in orbital parameters and by the 
   limitations imposed by display resolution. Orbits with higher inclinations, 
   as would be the case if near-polar launches from Vandenburg AFB in 
   California are ever initiated, would have much larger periodic errors which 
   would be both noticeable and objectionable. More important for longer 
   missions and for general satellite tracking is the fact that due to the 
   method used, errors in the orbital calculations tend to be cumulative. 
   Although it may be the only method available at launch, after about a week 
   the errors can become unacceptably large.
        The real problem with the simple method, of course, is that the Earth 
   is not a perfect sphere and actual satellite orbits are never perfectly 
   circular. Satellite orbits are significantly perturbed by the non-spherical
   gravitational field of the Earth, by the Sun and Moon, atmospheric drag, 
   and other factors. Accurate satellite tracking over longer periods of time 
   therefore demands more accurate data and a more rigorous treatment of 
   satellite orbits. The only practical alternative is to use the NASA/NORAD 
   2-line orbital element sets. Not only are these data readily available 
   publicly, but they are relatively accurate and are updated regularly. 2-
   line element sets for non-military space shuttle missions are typically 
   available by the second or third day of the mission. Amateur astronomers 
   and satellite tracking experts often generate "unofficial" 2-line element 
   sets even for military missions.
        Six quantities are required by classical gravitational theory to 
   completely characterize the orbit of one body about another in time and 
   space, the "Two Body Problem". These six quantities, often referred to as 
   Keplerian orbital elements, are included in the NASA/NORAD 2-line element 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 39


   sets along with other numerical and statistical data. NORAD, the North 
   American Air Defense Command headquartered in Cheyenne Mountain, Colorado, 
   developed the 2-line element format many years ago as part of their 
   satellite tracking efforts and NASA subsequently adopted the same format -- 
   more or less. My own analyses of 2-line element sets obtained independently 
   from other NASA centers indicate that NASA and NORAD do not always use the 
   same definition for revolution (orbit) numbers; NASA frequently gives a 
   number one greater than NORAD, calling the first partial orbit number one 
   while NORAD calls that same partial orbit number zero. Except for short 
   duration missions, such as the Space Shuttle, revolution numbers are of no 
   practical importance.
        Having timely and accurate orbital data is of little help without a 
   computer model or program which can use those data. NORAD has rather 
   arbitrarily divided satellite orbits into two categories: near Earth orbits 
   and deep space orbits. Near Earth orbits are defined as those with orbital 
   periods of 225 minutes or less and deep space orbits are all others. 
   Computer models are described in the literature for each category. STSORBIT 
   employs the SGP4 Near Earth Model only, using a composite of code of my own 
   combined with translated Fortran and Basic source supplied by Paul Traufler 
   and C source by Paul Hirose. Not only are the near Earth orbits generally 
   of more interest to observers, but the errors associated with deep space 
   orbits processed with the SGP4 model (rather than the correct SDP4 model) 
   are not particularly significant for the purposes of a program such as 
   STSORBIT. Further, watching a geostationary satellite orbit on the screen 
   is not unlike watching grass grow and is about as exciting.
        For the past several years, T S Kelso has been making the NASA/NORAD 
   data available as a public service on his Celestial BBS at (513) 427-0674. 
   The 2-line element sets are downloaded by Kelso directly from NASA Goddard 
   Space Flight Center by special arrangement. I regularly post a slightly 
   edited version (certain introductory text material is removed so that the 
   file may be used directly by programs such as STSORBIT) of the current 
   element sets on my own RPV ASTRONOMY BBS as file NASAnnn.TXT, where "nnn" 
   is the NASA bulletin number. Kelso provides data for several categories of 
   satellites:  Amateur Radio, Earth Resources, Manned Spacecraft, Navigation, 
   Weather, and NASA's 30 Day Specials (which contain objects launched within 
   the last 30 days and are often easy to spot visually). More specifically, 
   these include the following satellites or satellite series: OSCAR, Radio 
   Sputnik, UOSAT, Cosmos, LandSat, SeaSat 1, SPOT, Mir, Salyut 7, Soyuz, 
   Space Shuttle, NAVSTAR (GPS), GOES, Meteor, and NOAA.
        The Canadian Space Society BBS, (416) 458-5907, also regularly posts 
   NORAD 2-line elements. Note that the CSS format is slightly non-standard, 
   having additional information on the first (title) line for each satellite, 
   and may have to be edited for use with some tracking programs. The CSS 
   files also have considerable additional text material (including current 
   satellite news) before and after the actual 2-line elements data.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 40


   ADJUSTING ORBITAL PARAMETERS (Simple Orbital Model)
   ---------------------------------------------------

        NOTE: This section applies ONLY if you are using the simple orbital 
        model for simulation. When using 2-line elements, all orbital 
        parameters are completely defined by the 2-line elements and may not 
        be modified from within STSORBIT.

        The original "simple" orbital model used in STSORBIT is imperfect, to 
   say the least. The data generally available from NASA prior to launch often 
   does not describe upcoming shuttle orbits at all precisely. In particular, 
   STSORBIT's initial orbital calculations, those related to the time from 
   liftoff to orbital insertion, are more or less guesswork. Once a mission is 
   established in orbit, it may be therefore desirable to adjust the orbital 
   parameters to make STSORBIT's displayed ground track correspond more 
   closely to that displayed on the wall map in Mission Control Center. To 
   make the adjustment, use the following procedure:

   1.   Start program STSORBIT. After the map data has been read in, select 
        the program options command, F10, then press F5 to enable display of 
        the data for the ascending and descending nodes. Enter the original 
        launch time and orbital data using the F4 command or restore prior 
        data using the ENTER key or F3 command if no adjustments have been 
        entered. The plot will appear on the screen.

   2.   Observe the crossing time and longitude of the node of interest and 
        calculate the difference from the desired crossing time. Note that 
        NASA performs all orbital calculations referenced to the Ascending 
        Node, the point at which the ground track crosses the Equator in a 
        North-bound direction. In order to view a given node crossing 
        repeatedly, you may find it convenient to reset the DOS clock to a 
        minute or two prior to the expected time.

        HINT: Use the F9 command to go back to DOS, then use DOS's TIME 
        command to set the clock. BE SURE TO RESET YOUR COMPUTER CLOCK WHEN 
        YOU HAVE COMPLETED ALL ORBITAL ADJUSTMENTS!

   3.   When adjusting orbital parameters, it is preferable to adjust the TIME 
        before adjusting the LONGITUDE. This is because the longitude of the 
        node is affected by the rotation of the Earth (by 15 degrees per hour) 
        when the time is changed. Calculate the difference between the time of 
        the observed node crossing and the time of crossing plotted by 
        STSORBIT. If the observed time is earlier than the plotted time, the 
        time adjustment must be positive, otherwise it must be negative. The 
        time must be calculated in minutes and decimal fractions of a minute.

   4.   Press ENTER to return to the Main Menu, then press F5 to enter 
        adjusted data. Enter the new orbital altitude in nautical miles (or 
        altitude in kilometers by adding "km"); usually, the orbital altitude 
        has not changed and you should press ENTER to leave this item 
        unchanged.

   5.   Press ENTER to leave the longitude adjustment set at zero.

   6.   Enter the calculated time difference for the node crossing as the time 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 41


        adjustment (in minutes).

   7.   Press ENTER to leave the launch time unchanged.

   8.   Inspect the data displayed to be sure it is correct. If it is not, 
        press the SPACE BAR to re-enter data; if it is correct, press ENTER to 
        accept the data. STSORBIT will immediately begin plotting the new 
        ground track. If necessary, interrupt the plot with the ENTER key, 
        reset your computer's clock, return to STSORBIT, and press ENTER to 
        resume current mission.

   9.   Again observe the plotted time of crossing and repeat from Step 4 if 
        the time is not correct. If the time is correct, note the longitude of 
        the node and calculate the difference from the observed longitude. If 
        the plotted longitude is less than the observed longitude, the 
        adjustment must be positive, otherwise it must be negative. The 
        longitude adjustment must be entered in degrees and decimal fractions 
        of a degree.

   10.  Press ENTER to return to the Main Menu, then press F5 to enter 
        adjusted data. Enter the calculated longitude adjustment, then press 
        ENTER twice to leave the time adjustment and launch time unchanged.

   11.  Inspect the data displayed to be sure it is correct. If it is not, 
        press the SPACE BAR to re-enter data; if it is correct, press ENTER to 
        accept the data. STSORBIT will immediately begin plotting the new 
        ground track. If necessary, interrupt the plot with the ENTER key, 
        reset your computer's clock, return to STSORBIT, and press ENTER to 
        resume current mission.

   12.  This procedure should enable you to set the orbital parameters with 
        considerable accuracy. However, even minor changes of the orbit in 
        flight can cause a significant cumulative error in the ground track 
        displayed by STSORBIT. If all this seems like too much effort, just 
        enjoy the program "as it comes from the box"!

   13.  During the course of a non-military mission, I normally watch NASA 
        Select TV (if I'm around!) and post updated .INI files from time to 
        time on my BBS. You may call the BBS and download the updated .INI 
        files; these files typically have names such as STS31A.INI, STS31B.INI 
        and so forth. Use the F3 command to read the updated .INI file into 
        program STSORBIT. Also, within a day or two of a Space Shuttle launch, 
        the 2-line elements for the mission will usually be available on my 
        BBS.


   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 42


   STSORBIT REVISION HISTORY
   -------------------------

        Program STSORBIT underwent multiple revisions during the first days of 
   the STS-30 Atlantis/Magellan mission (May 1989) and the process was 
   repeated during the STS-28 Columbia mission (August 1989). At one point, I 
   was releasing new versions every couple of hours! Lacking any equations or 
   data for the first minutes of a typical mission, the first tries were 
   largely guesswork and needed to be refined considerably. After all of that, 
   comparison of STSORBIT's plot with the NASA wall map data (as seen on NASA 
   Select Television) and interpolation of that data shows good agreement 
   through about the first ten orbits. However, after orbital maneuvers, such 
   as occur with the deployment of a satellite or spacecraft, the initial data 
   is much less accurate. Unfortunately, the NASA wall map is not always on 
   the screen and orbital information may otherwise be difficult to obtain 
   during the first day or two of a mission.
        The launch of the Hubble Space Telescope (May 1990) and the 
   availability of the NASA/NORAD 2-Line Element Sets has prompted a major 
   revision of the program at Version 9022 to permit accurate tracking over 
   longer periods of time using these data. This has required a major rewrite 
   of the program which required many days of effort. As with any major 
   software change, not all problems and bugs are detected in the first 
   releases. User feedback and patience will be appreciated.
         Each released version of STSORBIT uses a four digit revision code 
   such as 9118. The first two digits indicate the year and the second two 
   digits indicate the week of the year. In some cases, an additional letter 
   suffix is added to distinguish changes occurring within the same week. A 
   partial week at the beginning or end of the year is counted as a full week. 
   Using this method, a year will typically have 53 weeks although it is 
   possible to have 54 weeks in a leap year (1972 is an example). The current 
   year-week revision code is shown on the Julian Date display, Display Mode 
   7, in my program ASTROCLK.
        This file records the revision history of program STSORBIT through all 
   of the minor twists and turns that usually accompany the evolution of such 
   a program.  It illustrates the tortuous process of maintaining and refining 
   a program as ideas and problems are reported from every quarter. The early 
   versions were rushed to meet the launch schedules, probably too much so. 
   These notes may also be helpful to users who are upgrading from one version 
   to another to find out what has changed.

                                                 David H. Ransom, Jr.


   9123     06/02/91
   -----------------
   -This version is a PERFORMANCE UPGRADE, especially for slow computers or 
   computers NOT equipped with a math coprocessor chip. I have tested this 
   version on my 80386/87 system and on my 8086 system (no math coprocessor) 
   in an effort to make most features available on all types of systems 
   without loss of real time tracking capability. Where practical, the 
   calculations have been distributed in time or the screen resolution has 
   been reduced in order to avoid a calculation overload "on the minute". 
   Users with a high speed computer equipped with a math coprocessor chip will 
   not notice a significant performance change.
   -Since most features are now available to all users, regardless of the 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 43


   monitor type and computer speed, it is up to the user to make sure that the 
   appropriate options are enabled or disabled. COMPUTERS NOT EQUIPPED WITH A 
   MATH COPROCESSOR SHOULD USE THE SLO MODE (F10+F7) TO KEEP THE GROUND TRACK 
   DISPLAY ACCURATE IN REAL TIME. For example, enabling the terminator on a 
   4.77 MHz XT-class computer without a math coprocessor will cause the ground 
   track to fall slowly behind real time. Check the minutes in the Simulation 
   and Local time displays at the lower left of the tracking display; if they 
   are not the same, your system is not able to keep up with real time with 
   the options selected. (The seconds may differ by as much as 5 seconds.)
   -The solar terminator is now available for all systems. The terminator is 
   partially updated every ten seconds to distribute the processing workload 
   more evenly. When the program is set to SLO (F10+F7), it will require a 
   full minute before the complete terminator is drawn on the screen. The 
   number of dots used to represent the terminator on the screen is adjusted 
   according to monitor type and whether or not the computer is using the SLO 
   mode.
   -The spacecraft circle of visibility is now available for all systems. When 
   the program is run in the normal mode, the circle of visibility is 
   recalculated every ten seconds for the actual spacecraft altitude. 
   Satellites with highly elliptical orbits will display a changing circle of 
   visibility. The local circle of visibility remains static, as calculated at 
   the moment the ground track display is started. Computers using the SLO 
   mode will also use a static circle of visibility, as calculated at the 
   moment the ground track display is started.

   9122C    05/31/91
   -----------------
   -This is a SPECIAL VERSION prepared for Warren James and radio station KPFK 
   in Los Angeles for their annual fund drive. NO TECHNICAL CHANGES FROM 
   VERSION 9122B.

   9122B    05/30/91
   -----------------
   -This is a SPECIAL VERSION prepared for the NASA/JPL Multimission Computer 
   Control Center. (Except for a special NASA/JPL title screen, all Version 
   9122B modifications are included in subsequent versions.)
   -The program now automatically substitutes the satellite name in the 
   mission title for HST, GRO, ROSAT, and MIR. The file name is omitted for 
   these special cases. The satellite names used in NASAnnn.TXT files and the 
   substituted names are:
        HST       Hubble Space Telescope
        GRO       Gamma Ray Observatory
        ROSAT     Roentgen Observatory
        MIR       MIR Soviet Space Stn
   Note that the original satellite abbreviation (as shown at the left above) 
   must still be used when searching the NASAnnn.TXT file.
   -Corrected an error in the satellite lighting subroutine that caused the 
   satellite to show an excessive penumbra and refraction lighting. (A 
   variable name typo!) Thanks to Paul Traufler and Ron Lafon for reporting 
   the error!
   -Corrected a problem that caused QuickBASIC Error 5 if the 2-line element 
   file was edited to create a long satellite name like "Hubble Space 
   Telescope". If the satellite name is longer than 10 characters, the full 
   name as read from the file is used and the file name, usually included in 
   square brackets, is omitted. The name is limited to 22 characters and will 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 44


   be truncated if longer. Note also that STSORBIT keys on "STS", "HST", 
   "GRO", and "MIR" as the leftmost three characters of the satellite name in 
   the file in order to enable the spacecraft circle of visibility. Thanks to 
   Charles White at the JPL Multimission Computer Control Center for reporting 
   the problem.
   -Corrected the version number on the help screen.

   9122A    05/27/91
   -----------------
   -This is a minor fix for HERCULES USERS. The persistent bug that caused the 
   program to halt with an error message unless the "/M" command line option 
   was included has, I hope, finally been found and fixed.
   -There are no other differences from Version 9122.

   9122     05/23/91
   -----------------
   -This is a MAJOR UPGRADE to the program. Version 9022 incorporates new 
   features tested in Beta Version 9021 (see also below) as well as other new 
   features added as a result of testing that version and user suggestions.
   -Added on-line help during the ground track display and changed the keys 
   used during that display to Function Keys. The following keys are active 
   during the ground track display:
      F1  Resume Data          F6  Pause Display            During PAUSE:
      F2  Satellite Blink      F7  Circle of Visibility     +  Move Forward
      F3  Printer Logging      F8  SUN and Terminator       -  Move Backward
      F4  Time Step            F9  Distance Units
      F5  MET/T+Epoch         F10  Satelitte Coordinates
   (Although the "old" individual letter keys are still active, they will be 
   discontinued in subsequent versions and only the Function Keys will be 
   used.) Thanks to Mike Gardner and others for their persistent requests for 
   the help screen.
   -In response to numerous requests, I have added the SUN and the solar 
   terminator to the ground track display (solar terminator only for CGA). The 
   Sun is shown as a yellow circle at the subsolar point and the terminator is 
   shown as a series of yellow dots marking the points at which the center of 
   the sun is at the horizon for observers at mean sea level; both features 
   are updated every 60 seconds. Toggle this display feature using F10+F3+F8 
   from the Main Menu (which also selects the spacecraft lighting effect for 
   EGA/VGA systems). The additional calculation time is substantial and this 
   feature may not be suitable for slow processors or computers without math 
   coprocessors. This feature is automatically disabled if the SLOW flag is 
   set. Thanks to Rob Matson for providing example code for the terminator.
   -Changed map file to STSORBIT.MPT and changed method of loading map data to 
   eliminate the prior time consuming method. Map file now loads with a single 
   disk access. If the /R command line option is given, the title screen will 
   then appear for two seconds; otherwise, the title screen will appear for 15 
   seconds. Press any key to continue immediately.
   -The spacecraft circle of visibility may be added to or removed from the 
   ground track display using Function Key F7. In prior versions, this could 
   only be accomplished from the menus. This feature is now also available on 
   CGA and HGC systems.
   -The SUN and terminator may be added to or removed from the ground track 
   display using Function Key F8. In prior versions, this could only be 
   accomplished from the menus.
   -Distance units may be switched between kilometers (km) and nautical miles 

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 45


   (nm) using Function Key F9.
   -Satellite coordinates may be switched between Altitude and Azimuth, Right 
   Ascension, and Geocentric Rectangular coordinates using Function Key F10.
   -Added Geocentric Rectangular satellite coordinates: SatX, SatY and SatZ 
   set by F10+F3+F10. Switch between nautical miles (nm) and kilometers (km) 
   using F10+F3+F9. NOTE: XYZ coordinates are available only with 2-line 
   orbital elements.
   -Corrected a bug in the Hubble Space Telescope icon (used for all non-space 
   shuttle missions) which caused it to be displayed incorrectly; right place 
   but faulty icon.
   -Spacecraft circle of visibility is now allowed for Hubble Space Telescope 
   (HST), Gamma Ray Observatory (GRO), and the Soviet MIR Space Station (MIR) 
   in addition to space shuttle missions.
   -Fixed bug that caused minor error after demo. Program now rereads the .INI 
   file after demo to correctly restore all data.
   -Sun and terminator now displayed for simple orbital model prior to launch 
   time.

   9121     05/21/91
   -----------------
   -This is a non-public BETA RELEASE to test several new features. 
   -Repaired minor bug when switching between MET and T+EPOCH which caused 
   that time data to be incorrect for one calculation cycle.
   -Repaired bug with HGC displays that required the use of the /M command 
   line option for Version 9118. HGC systems should now operate correctly 
   without the /M command line option.

   9118     04/29/91
   -----------------
   -Moved Display Features to a new sub-menu on Program Options using Function 
   Key F3. All options are now saved in the .INI file.
   -Shuttle circle of visibility now an option in Display Features menu for 
   EGA/CGA monitors.
   -Added satellite coordinates in topocentric Right Ascension and Declination 
   (R/D) on Display Features menu. Coordinates may now be displayed as either 
   Altitude/Azimuth (A/A) or RightAscension/Declination (R/D), referenced to 
   the local coordinates as of the epoch of date.
   -Added distance toggle between nautical miles and kilometers on Display 
   Features menu.
   -Added feature to display the location and circle of visibility for a 
   second city. Select F10 for Program Options and Features, then F2 for Local 
   Coordinates and proceed as usual. When you have selected or entered the 
   name and coordinate information for the second city, press TAB to ACCEPT. 
   To clear the second city, press F10+F2, then "*" for manual data entry, 
   enter SPACE (press only the SPACE BAR followed by ENTER) as the city name, 
   press ENTER for the coordinates and elevation, then TAB to clear the second 
   city.
   -When used with a CGA monitor (or when CGA mode is forced with the /CGA 
   command line option), the text screens are now in color. To display all 
   screens in monochrome on the CGA, use the /M command line option. Note that 
   whether or not color is used for text, GRAPHICS (the map and ground track) 
   will ALWAYS be in monochrome for CGA monitors!
   -Split main source code into two modules for compiler memory problems.

   STSORBIT Space Shuttle and Satellite Orbit Simulation              Page 46


   9117     04/27/91
   -----------------
   -Corrected a serious typographical error introduced in Version 9116. The 
   program would not execute with HGC or CGA monitors.
   -EGA and VGA monitors now display the SAA (South Atlantic Anomaly) in white 
   between South America and the tip of Africa. This is a rough approximation 
   of the area of the SAA.
   -Added capability to display the location and circle of visibility of a 
   second location. Use F2 as you would for changing local coordinates except 
   press TAB instead of ENTER for this feature. Enter a city name of one or 
   more spaces, then use TAB to disable this feature. Thanks to several users 
   for this suggestion.

   9116     04/18/91
   -----------------
   -Added code to detect an EGA equipped with a MONOCHROME monitor, QuickBASIC 
   screen mode 10. (Thanks to Brian Kornfeld for reporting the problem.)

   9114     04/03/91
   -----------------
   -Corrected a problem with Version 9112 (and probably 9049 as well) which 
   caused an incorrect date to be entered with Main Menu F4. No matter what 
   date was entered, the date appeared as the year 4713. The following will 
   work around the problem for Version 9112: Accept the "bad" date, then press 
   F5 to adjust the launch date to the desired date.

   9112     03/30/91
   -----------------
   -Added calculations to determine if the satellite is sunlit (2-line element 
   mode ONLY). Special thanks to Rob Matson for his assistance! The satellite 
   color changes depending upon the lighting (EGA and VGA):
        Light White    Fully lighted
        Yellow         Penumbra (including Refracted Sunlight)
        White          Umbra

   9049     12/04/90
   -----------------
   -Added spacecraft circle of visibility for STS missions, EGA/VGA ONLY!
   -Corrected the logic associated with printer logging so that TDRS Com: data 
   is properly updated when logging is ON. Thanks to Jay Hickman for reporting 
   the bug!
   -Corrected negative Mission Elapsed Time (MET) in both orbital models. Time 
   BEFORE launch time and date was incorrect.
   -Changed MET input routine (F8+F4) to allow negative MET dates and times. I 
   don't really know why anyone would want this, but ...
   -Program now saves presence/absence of additional grid in STSORBIT.INI.
   -Documentation updated to reflect program changes and additions. The 
   description of the ground track display has been rewritten for improved
   clarity.

   [Intermediate revision notes removed to save space. Available on request.]

   8916      4/24/89 
   -----------------
   -Initial BETA VERSION Release.