Documentation for PRIVATE REPLACEMENT for OS2DASD.DMD

    The enclosed OS2DASD.DMD is a replacement for the OS/2 2.1 OS2DASD.DMD.
    It should only be used if your system exhibits the problem described
    in this document.

    THE PROBLEM:

    OS/2 2.0 created a "logical disk geometry" that included "spare"
    sectors at the end of the drive.  There were not enough "spare"
    sectors to make a full track, due to the differences between the
    physical and logical geometries.  A few systems would not be able
    to format these spare sectors (because FORMAT wants to format an
    entire track at a time), so in OS/2 2.1, these spare sectors are not
    given to the system.

    If you used OS/2 2.0 FDISK to partition the drive, and install OS/2 2.1,
    and you have spare sectors, they will not be visible to programs that
    use disk IOCtls to access the data.  Only FORMAT and CHKDSK (and other
    3rd party utilities) use this method.  The only time this will cause
    a problem is if the LAST partition on the drive is HPFS.  Since HPFS
    puts system information that CHKDSK uses on the last sector of a drive,
    CHKDSK will fail if OS/2 2.1 does not allow IOCtl access to the last
    sector.

    If the last partition on your drive is an HPFS partition, run CHKDSK
    on that partition (WITHOUT the /F switch).  If CHKDSK returns error
    SYS0551, you probably have this problem.

    THE SOLUTION:

    The enclosed OS2DASD.DMD will allow CHKDSK and other IOCtl-based
    utilities to access the entire disk.  Save the OS2DASD.DMD that is
    in the \OS2 directory of your boot drive, and replace it with the
    enclosed OS2DASD.DMD, and restart your computer.  CHKDSK should now
    run without a SYS0551 error.