{
 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

 Visionix Serial Communictions LOW Unit (VSER)
 Copyright 1991,92,93 Visionix
 ALL RIGHTS RESERVED

 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 revision history in reverse chronological order:

 Initials  Date      Comment

 ÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 lpg       03/16/93  Added Source Documentation

 mep       02/11/93  Cleaned up code for beta release

 jrt       02/08/93  Sync with beta 0.12 release

 jrt       11/21/92  Sync with beta 0.08

 jrt       09/01/92  First logged revision.

 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
}



Unit VSerLow;


CONST

  {-------------------------}
  { Serial Driver Functions }
  {-------------------------}

  sdfDriverNew        = 1;
  sdfDriverOff        = 2;
  sdfDriverOn         = 3;
  sdfDriverDispose    = 4;
  sdfActivatePort     = 5;
  sdfDeActivatePort   = 6;
  sdfSetCommParam     = 7;
  sdfGetCommParam     = 8;
  sdfGetFlowConType   = 9;
  sdfSetFlowConType   = 10;
  sdfTurnSendOnOff    = 11;
  sdfTurnReceiveOnOff = 12;
  sdfBreakOnOff       = 13;
  sdfDTROnOff         = 14;
  sdfGetStatus        = 15;
  sdfFlushOutBuff     = 16;
  sdfPurgeOutBuff     = 17;
  sdfPurgeInBuff      = 18;
  sdfEventProcNew     = 19;
  sdfEventProcOff     = 20;
  sdfEventProcOn      = 21;
  sdfEventProcDispose = 22;
  sdfWriteCh          = 23;
  sdfWriteBlock       = 24;
  sdfReadCh           = 25;
  sdfReadBlock        = 26;

  {-------------------------}

  {----------------------------------------}
  { Modem Status Register status bits (AL) }
  {----------------------------------------}

  MSRctsDelta = $01; { Clear To Send changed                                 }
                     { Delta CTS - not reliable                              }
  MSRdsrDelta = $02; { Data Set Ready changed                                }
                     { Delta DSR - not reliable                              }
  MSRriDelta  = $04; { Ring Indicate changed                                 }
                     { Delta DCD - not reliable                              }
  MSRcdDelta  = $08; { Carrier Detect changed                                }
                     { always set to 1 upon return (DUMMY DCD)               }
  MSRcts      = $10; { Clear To Send                                         }
                     { CTS - DCE sets - do not xmit until true               }
  MSRdsr      = $20; { Data Set Ready                                        }
                     { DSR - modem is ready to be used                       }
  MSRri       = $40; { Ring Indicate                                         }
                     { RI - only on during active voltage signal             }
  MSRcd       = $80; { Carrier Detect                                        }
                     { DCD - data carrier detect                             }

  {---------------------------------------}
  { Line Status Register status bits (AH) }
  {---------------------------------------}

  LSRRcvReady = $01; { Received data ready                                   }
                     { RDA  - input data is available in buffer              }
  LSROverrun  = $02; { OverRun error                                         }
                     { OVRN - the input buffer has been overrun              }
  LSRParity   = $04; { Parity error                                          }
                     { Reserved (Parity error in BIOS INT 14h)               }
  LSRFrame    = $08; { Framing error                                         }
                     { Reserved (Framing error in BIOS INT 14h)              }
  LSRBreak    = $10; { Break detected                                        }
                     { Reserved (Break detect in BIOS INT 14h)               }
  LSRXhReady  = $20; { Transmit hold register empty                          }
                     { THRE - room is available in output buffer             }
  LSRXsReady  = $40; { Transmit shift register empty                         }
                     { TSRE - output buffer is empty                         }
  LSRTimeout  = $80; { Timeout (software implemented).  If true,             }
                     { then none of the above 15 bits are valid.             }

  {-----------------------------}
  { Modem Control Register bits }
  {-----------------------------}

  MCRDtr      = $1; { Data terminal ready                                    }
  MCRRts      = $2; { Request to send                                        }
  MCROut1     = $4; { Out1: software implemented output                      }
  MCROut2     = $8; { Out2: as Out1 with interrupts to system-bus            }
  MCRLoop     = $10;{ Loopback test mode                                     }

  {----------------------------}
  { Line Control Register bits }
  {----------------------------}

  LCRdatabits = $1; { Bits/character (databits) - bits 1-0                   }
  LCRstopbits = $4; { Stop bits of character                                 }
  LCRparity   = $8; { Parity - bits 5-3                                      }
  LCRbreak    = $20;{ Enable break status                                    }
  LCRdivisor  = $40;{ Enable addressing of baudrate divisor registers        }

  {----------------------------------------}
  { Interrupt Identification Register bits }
  {----------------------------------------}

  IIRReady    = $1; { Interrupt waiting status                               }

  {---------------------------}
  { Interrupt Enable Register }
  {---------------------------}

  IEREnabRE   = $1; { Enable read (receive data) interrupt status            }
  IEREnabWI   = $2; { Enable write (transmit empty) register interrupt       }
  IEREnabLSR  = $4; { Enable line status interrupt                           }
  IEREnabMSR  = $8; { Enable delta modem status interrupt                    }

  {------------------------------------------------------}
  { Serial Registers - These are the offsets from IOPort }
  {------------------------------------------------------}

  DLL = 0;  { Divisor Latch Least-significant-byte (LCR bit $80 on)          }
  DLM = 1;  { Divisor Latch Most-significant-byte (LCR bit $80 on)           }
  RBR = 0;  { Receiver Buffer Register (read)                                }
  THR = 0;  { Transmitter Holding Register (write)                           }
  IER = 1;  { Interrupt Enable Register                                      }
  IIR = 2;  { Interrupt Identification Register (read only)                  }
  LCR = 3;  { Line Control Register                                          }
  MCR = 4;  { Modem Control Register  (see above)                            }
  LSR = 5;  { Line Status Register  (see above)                              }
  MSR = 6;  { Modem Status Register  (see above)                             }
  SPR = 7;  { 8250 Scratch Pad Register                                      }

  {------------------------}
  { MISCELLANOUS CONSTANTS }
  {------------------------}

  IMR      = $21; { Port address of the Interrupt Mask Register              }

  NUL   = #0;  {^@}     SOH   = #1;  {^A}     STX   = #2;  {^B}
  ETX   = #3;  {^C}     EOT   = #4;  {^D}     ENQ   = #5;  {^E}
  ACK   = #6;  {^F}     BEL   = #7;  {^G}     BS    = #8;  {^H}
  HT    = #9;  {^I}     LF    = #10; {^J}     VT    = #11; {^K}
  FF    = #12; {^L}     CR    = #13; {^M}     SO    = #14; {^N}
  SI    = #15; {^O}     DLE   = #16; {^P}     DC1   = #17; {^Q}
  DC2   = #18; {^R}     DC3   = #19; {^S}     DC4   = #20; {^T}
  NAK   = #21; {^U}     SYN   = #22; {^V}     ETB   = #23; {^W}
  CAN   = #24; {^X}     EM    = #25; {^Y}     SUB   = #26; {^Z}
  ESC   = #27;          FS    = #28; {^\}     GS    = #29; {^`}
  RS    = #30; {^=}     US    = #31; {^-}     SP    = #32;
  DEL   = #127;         BLANK = #255;       


Type

  PCommParam = ^TCommParam;
  TCommParam = RECORD

    ComPort   : BYTE;
    BaudRate  : LONGINT;
    Parity    : CHAR;
    DataBits  : BYTE;
    StopBits  : BYTE;

    Break     : BOOLEAN;

  END;

  PSerDriverPacket = ^TSerDriverPacket;
  TSerDriverProc   = Procedure( SDPacket : PSerDriverPacket );
  PSerDriverProc   = ^TSerDriverProc;
  TSerDriverPacket = RECORD

    Func            : WORD;
    IData           : POINTER;
    SerDriverProc   : TSerDriverProc;
    DriverInfo      : POINTER;

    CommParam       : PCommParam;
    FlowConType     : INTEGER;
    OnOff           : BOOLEAN;
    Status          : LONGINT;
    Error           : LONGINT;
  { EventProc       : TSerEventProc;
    EventMask       : WORD;
    EventProcInfo   : POINTER;
    EventProcHandle : TSerEventProcHandle; }
    Ch              : CHAR;
    Buf             : POINTER;
    Count           : LONGINT;
    Result          : LONGINT;

  END;

  PSerChan = ^TSerChan;

  TSerChan = RECORD

    Sig              : WORD;
    SerDriverProc    : TSerDriverProc;
    SerDriverID      : POINTER;
  { EventProcList    : ... }
    SDP              : TSerDriverPacket;

  END;



  PSerCaps = ^TSerCaps;
  TSerCaps = RECORD

    A : WORD;

  END;


{ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ}

Procedure VSerLowBIOSInfo(             ComPort       : BYTE;
                                   Var IOPort        : WORD;
                                   Var IRQ           : BYTE;
                                   Var IntNo         : BYTE    );



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


[FUNCTION]

Procedure VSerLowBIOSInfo(             ComPort       : BYTE;
                                   Var IOPort        : WORD;
                                   Var IRQ           : BYTE;
                                   Var IntNo         : BYTE    );

[PARAMETERS]

ComPort     Communications Port Number
IOPort      VAR Returned IO Port Number
IRQ         VAR Returned IRQ Number
IntNo       VAR Returned Interrupt Number

[RETURNS]

Function : None
(VAR     : [IOPort] IO Port Number)
(VAR     : [IRQ] Returned IRQ Number)
(VAR     : [IntNo] Returned Interrupt Number)

[DESCRIPTION]

[SEE-ALSO]

[EXAMPLE]